INTERNATIONAL STANDARD ISO/IEC 8652:1995(E)















INFORMATION TECHNOLOGY -- PROGRAMMING LANGUAGES -- ADA

[Revision of first edition (ISO 8652:1987)]

                                  ANNOTATED
                            ADA REFERENCE MANUAL


                       Language and Standard Libraries

                                Version 5.95
                              25 November 1994








Copyright (C) 1992,1993,1994,1995  Intermetrics, Inc.

This copyright is assigned to the U.S. Government.  All rights reserved.

This document may be copied, in whole or in part, in any form or by any
means, as is or with alterations, provided that (1) alterations are clearly
marked as alterations and (2) this copyright notice is included unmodified in
any copy.  Compiled copies of standard library units and examples need not
contain this copyright notice so long as the notice is included in all copies
of source code and documentation.
INTERNATIONAL ORGANIZATION FOR STANDARDIZATION
INTERNATIONAL ELECTROTECHNICAL COMMISSION
Foreword


1   ISO (the International Organization for Standardization) and IEC (the
International Electrotechnical Commission) form the specialized system for
worldwide standardization.  National bodies that are members of ISO or IEC
participate in the development of International Standards through technical
committees established by the respective organization to deal with particular
fields of technical activity.  ISO and IEC technical committees collaborate
in fields of mutual interest.  Other international organizations,
governmental and non-governmental, in liaison with ISO and IEC, also take
part in the work.

2   In the field of information technology, ISO and IEC have established a
joint technical committee, ISO/IEC JTC 1.  Draft International Standards
adopted by the joint technical committee are circulated to national bodies
for voting.  Publication as an International Standard requires approval by at
least 75 % of the national bodies casting a vote.

3   International Standard ISO/IEC 8652 was prepared by Joint Technical
Committee ISO/IEC JTC 1, Information Technology.

4   This second edition cancels and replaces the first edition (ISO
8652:1987), of which it constitutes a technical revision.

5   Annexes A to J form an integral part of this International Standard.
Annexes K to P are for information only.

        5.a   Change:  Changed Annex letters as per instructions from ISO.

        5.b   Discussion:  This document is the Annotated Ada Reference
        Manual (AARM).  It contains the entire text of the Ada 9X standard
        (ISO/IEC 8652:1995(E)), plus various annotations.  It is intended
        primarily for compiler writers, validation test writers, and other
        language lawyers.  The annotations include detailed rationale for
        individual rules and explanations of some of the more arcane
        interactions among the rules.
Introduction


1   This is the Annotated Ada Reference Manual.

2   Other available Ada documents include:

    3  Rationale for the Ada Programming Language -- 1995 edition, which
       gives an introduction to the new features of Ada, and explains
       the rationale behind them.  Programmers should read this first.

    4  The Ada Reference Manual (RM).  This is the International
       Standard -- ISO/IEC 8652:1995(E).

    5  Changes to Ada -- 1987 to 1995.  This document lists in detail
       the changes made to the 1987 edition of the standard.


Design Goals

6   Ada was originally designed with three overriding concerns:  program
reliability and maintenance, programming as a human activity, and efficiency.
This revision to the language was designed to provide greater flexibility and
extensibility, additional control over storage management and synchroniza-
tion, and standardized packages oriented toward supporting important
application areas, while at the same time retaining the original emphasis on
reliability, maintainability, and efficiency.

7   The need for languages that promote reliability and simplify maintenance
is well established.  Hence emphasis was placed on program readability over
ease of writing.  For example, the rules of the language require that program
variables be explicitly declared and that their type be specified.  Since the
type of a variable is invariant, compilers can ensure that operations on
variables are compatible with the properties intended for objects of the
type.  Furthermore, error-prone notations have been avoided, and the syntax
of the language avoids the use of encoded forms in favor of more English-like
constructs.  Finally, the language offers support for separate compilation of
program units in a way that facilitates program development and maintenance,
and which provides the same degree of checking between units as within a
unit.

8   Concern for the human programmer was also stressed during the design.
Above all, an attempt was made to keep to a relatively small number of
underlying concepts integrated in a consistent and systematic way while
continuing to avoid the pitfalls of excessive involution.  The design
especially aims to provide language constructs that correspond intuitively to
the normal expectations of users.

9   Like many other human activities, the development of programs is becoming
ever more decentralized and distributed.  Consequently, the ability to
assemble a program from independently produced software components continues
to be a central idea in the design.  The concepts of packages, of private
types, and of generic units are directly related to this idea, which has
ramifications in many other aspects of the language.  An allied concern is
the maintenance of programs to match changing requirements; type extension
and the hierarchical library enable a program to be modified while minimizing
disturbance to existing tested and trusted components.

10   No language can avoid the problem of efficiency.  Languages that require
over-elaborate compilers, or that lead to the inefficient use of storage or
execution time, force these inefficiencies on all machines and on all
programs.  Every construct of the language was examined in the light of
present implementation techniques.  Any proposed construct whose
implementation was unclear or that required excessive machine resources was
rejected.


Language Summary

11   An Ada program is composed of one or more program units.  Program units
may be subprograms (which define executable algorithms), packages (which
define collections of entities), task units (which define concurrent
computations), protected units (which define operations for the coordinated
sharing of data between tasks), or generic units (which define parameterized
forms of packages and subprograms).  Each program unit normally consists of
two parts:  a specification, containing the information that must be visible
to other units, and a body, containing the implementation details, which need
not be visible to other units.  Most program units can be compiled
separately.

12   This distinction of the specification and body, and the ability to
compile units separately, allows a program to be designed, written, and
tested as a set of largely independent software components.

13   An Ada program will normally make use of a library of program units of
general utility.  The language provides means whereby individual
organizations can construct their own libraries.  All libraries are
structured in a hierarchical manner; this enables the logical decomposition
of a subsystem into individual components.  The text of a separately compiled
program unit must name the library units it requires.

14   Program Units

15   A subprogram is the basic unit for expressing an algorithm.  There are
two kinds of subprograms: procedures and functions.  A procedure is the means
of invoking a series of actions.  For example, it may read data, update
variables, or produce some output.  It may have parameters, to provide a
controlled means of passing information between the procedure and the point
of call.  A function is the means of invoking the computation of a value.  It
is similar to a procedure, but in addition will return a result.

16   A package is the basic unit for defining a collection of logically
related entities.  For example, a package can be used to define a set of type
declarations and associated operations.  Portions of a package can be hidden
from the user, thus allowing access only to the logical properties expressed
by the package specification.

17   Subprogram and package units may be compiled separately and arranged in
hierarchies of parent and child units giving fine control over visibility of
the logical properties and their detailed implementation.

18   A task unit is the basic unit for defining a task whose sequence of
actions may be executed concurrently with those of other tasks.  Such tasks
may be implemented on multicomputers, multiprocessors, or with interleaved
execution on a single processor.  A task unit may define either a single
executing task or a task type permitting the creation of any number of
similar tasks.

19   A protected unit is the basic unit for defining protected operations for
the coordinated use of data shared between tasks.  Simple mutual exclusion is
provided automatically, and more elaborate sharing protocols can be defined.
A protected operation can either be a subprogram or an entry.  A protected
entry specifies a Boolean expression (an entry barrier) that must be true
before the body of the entry is executed.  A protected unit may define a
single protected object or a protected type permitting the creation of
several similar objects.

20   Declarations and Statements

21   The body of a program unit generally contains two parts: a declarative
part, which defines the logical entities to be used in the program unit, and
a sequence of statements, which defines the execution of the program unit.

22   The declarative part associates names with declared entities.  For
example, a name may denote a type, a constant, a variable, or an exception.
A declarative part also introduces the names and parameters of other nested
subprograms, packages, task units, protected units, and generic units to be
used in the program unit.

23   The sequence of statements describes a sequence of actions that are to
be performed.  The statements are executed in succession (unless a transfer
of control causes execution to continue from another place).

24   An assignment statement changes the value of a variable.  A procedure
call invokes execution of a procedure after associating any actual parameters
provided at the call with the corresponding formal parameters.

25   Case statements and if statements allow the selection of an enclosed
sequence of statements based on the value of an expression or on the value of
a condition.

26   The loop statement provides the basic iterative mechanism in the
language.  A loop statement specifies that a sequence of statements is to be
executed repeatedly as directed by an iteration scheme, or until an exit
statement is encountered.

27   A block statement comprises a sequence of statements preceded by the
declaration of local entities used by the statements.

28   Certain statements are associated with concurrent execution.  A delay
statement delays the execution of a task for a specified duration or until a
specified time.  An entry call statement is written as a procedure call
statement; it requests an operation on a task or on a protected object,
blocking the caller until the operation can be performed.  A called task may
accept an entry call by executing a corresponding accept statement, which
specifies the actions then to be performed as part of the rendezvous with the
calling task.  An entry call on a protected object is processed when the
corresponding entry barrier evaluates to true, whereupon the body of the
entry is executed.  The requeue statement permits the provision of a service
as a number of related activities with preference control.  One form of the
select statement allows a selective wait for one of several alternative
rendezvous.  Other forms of the select statement allow conditional or timed
entry calls and the asynchronous transfer of control in response to some
triggering event.

29   Execution of a program unit may encounter error situations in which
normal program execution cannot continue.  For example, an arithmetic
computation may exceed the maximum allowed value of a number, or an attempt
may be made to access an array component by using an incorrect index value.
To deal with such error situations, the statements of a program unit can be
textually followed by exception handlers that specify the actions to be taken
when the error situation arises.  Exceptions can be raised explicitly by a
raise statement.

30   Data Types

31   Every object in the language has a type, which characterizes a set of
values and a set of applicable operations.  The main classes of types are
elementary types (comprising enumeration, numeric, and access types) and
composite types (including array and record types).

32   An enumeration type defines an ordered set of distinct enumeration
literals, for example a list of states or an alphabet of characters.  The
enumeration types Boolean, Character, and Wide_Character are predefined.

33   Numeric types provide a means of performing exact or approximate
numerical computations.  Exact computations use integer types, which denote
sets of consecutive integers.  Approximate computations use either fixed
point types, with absolute bounds on the error, or floating point types, with
relative bounds on the error.  The numeric types Integer, Float, and Duration
are predefined.

34   Composite types allow definitions of structured objects with related
components.  The composite types in the language include arrays and records.
An array is an object with indexed components of the same type.  A record is
an object with named components of possibly different types.  Task and
protected types are also forms of composite types.  The array types String
and Wide_String are predefined.

35   Record, task, and protected types may have special components called
discriminants which parameterize the type.  Variant record structures that
depend on the values of discriminants can be defined within a record type.

36   Access types allow the construction of linked data structures.  A value
of an access type represents a reference to an object declared as aliased or
to an object created by the evaluation of an allocator.  Several variables of
an access type may designate the same object, and components of one object
may designate the same or other objects.  Both the elements in such linked
data structures and their relation to other elements can be altered during
program execution.  Access types also permit references to subprograms to be
stored, passed as parameters, and ultimately dereferenced as part of an
indirect call.

37   Private types permit restricted views of a type.  A private type can be
defined in a package so that only the logically necessary properties are made
visible to the users of the type.  The full structural details that are
externally irrelevant are then only available within the package and any
child units.

38   From any type a new type may be defined by derivation.  A type, together
with its derivatives (both direct and indirect) form a derivation class.
Class-wide operations may be defined that accept as a parameter an operand of
any type in a derivation class.  For record and private types, the
derivatives may be extensions of the parent type.  Types that support these
object-oriented capabilities of class-wide operations and type extension must
be tagged, so that the specific type of an operand within a derivation class
can be identified at run time.  When an operation of a tagged type is applied
to an operand whose specific type is not known until run time, implicit
dispatching is performed based on the tag of the operand.

39   The concept of a type is further refined by the concept of a subtype,
whereby a user can constrain the set of allowed values of a type.  Subtypes
can be used to define subranges of scalar types, arrays with a limited set of
index values, and records and private types with particular discriminant
values.

40   Other Facilities

41   Representation clauses can be used to specify the mapping between types
and features of an underlying machine.  For example, the user can specify
that objects of a given type must be represented with a given number of bits,
or that the components of a record are to be represented using a given
storage layout.  Other features allow the controlled use of low level,
nonportable, or implementation-dependent aspects, including the direct
insertion of machine code.

42   The predefined environment of the language provides for input-output and
other capabilities (such as string manipulation and random number generation)
by means of standard library packages.  Input-output is supported for values
of user-defined as well as of predefined types.  Standard means of
representing values in display form are also provided.  Other standard
library packages are defined in annexes of the standard to support systems
with specialized requirements.

43   Finally, the language provides a powerful means of parameterization of
program units, called generic program units.  The generic parameters can be
types and subprograms (as well as objects and packages) and so allow general
algorithms and data structures to be defined that are applicable to all types
of a given class.


Language Changes

44   This International Standard replaces the first edition of 1987.  In this
edition, the following major language changes have been incorporated:

   45  Support for standard 8-bit and 16-bit character sets.  See
       Section 2, 3.5.2, 3.6.3, A.1, A.3, and A.4.

   46  Object-oriented programming with run-time polymorphism.  See the
       discussions of classes, derived types, tagged types, record
       extensions, and private extensions in clauses 3.4, 3.9, and 7.3.
       See also the new forms of generic formal parameters that are
       allowed by 12.5.1, ``Formal Private and Derived Types'' and 12.7,
       ``Formal Packages''.

   47  Access types have been extended to allow an access value to
       designate a subprogram or an object declared by an object
       declaration (as opposed to just a heap-allocated object).  See
       3.10.

   48  Efficient data-oriented synchronization is provided via protected
       types.  See Section 9.

   49  The library units of a library may be organized into a hierarchy
       of parent and child units.  See Section 10.

   50  Additional support has been added for interfacing to other
       languages.  See Annex B.

   51  The Specialized Needs Annexes have been added to provide specific
       support for certain application areas:

          52  Annex C, ``Systems Programming''

          53  Annex D, ``Real-Time Systems''

          54  Annex E, ``Distributed Systems''

          55  Annex F, ``Information Systems''

          56  Annex G, ``Numerics''

          57  Annex H, ``Safety and Security''

58   For a more detailed list of changes, see the Changes to Ada -- 1987 to
1995 document.
Instructions for Comment Submission

59   {instructions for comment submission} {comments, instructions for
submission} Informal comments on this International Standard may be sent via
e-mail to ada-comment@sei.cmu.edu.  If appropriate, the Project Editor will
initiate a Technical Corrigendum to be issued for the standard.

60   Comments should use the following format:

61
         !topic Title summarizing comment
         !reference RM95-ss.ss(pp)
         !from Author Name yy-mm-dd
         !keywords keywords related to topic
         !discussion

         text of discussion

        61.a   Change:  Removed ";5.95" from the !reference line.

62   where ss.ss is the section, clause or subclause number, pp is the
paragraph number where applicable, and yy-mm-dd is the date the comment was
sent.  The date is optional, as is the !keywords line.

63   Multiple comments per e-mail message are acceptable.  Please use a
descriptive ``Subject'' in your e-mail message.

64   When correcting typographical errors or making minor wording
suggestions, please put the correction directly as the topic of the comment;
use square brackets [ ] to indicate text to be omitted and curly braces { }
to indicate text to be added, and provide enough context to make the nature
of the suggestion self-evident or put additional information in the body of
the comment, for example:

65
         !topic [c]{C}haracter
         !topic it[']s meaning is not defined

66   Formal requests for interpretations and for reporting defects in this
International Standard may be made in accordance with the ISO/IEC JTC1
Directives and the ISO/IEC JTC1/SC22 policy for interpretations.  ISO Member
Bodies may submit a Defect Report to ISO for resolution under the JTC1 and
JTC1/SC22 procedures.  A response will be provided and, if appropriate, a
Technical Corrigendum will be issued through JTC1.
Acknowledgements

67   This International Standard was prepared by the Ada 9X Mapping/Revision
Team based at Intermetrics, Inc., which has included:  W. Carlson, Program
Manager; T. Taft, Technical Director; J. Barnes (consultant); B. Brosgol
(consultant); R. Duff (Oak Tree Software); M. Edwards; C. Garrity;
R. Hilliard; O. Pazy (consultant); D. Rosenfeld; L. Shafer; W. White;
M. Woodger.

68   The following consultants to the Ada 9X Project contributed to the
Specialized Needs Annexes:  T. Baker (Real-Time/Systems Programming -- SEI,
FSU); K. Dritz (Numerics -- Argonne National Laboratory); A. Gargaro
(Distributed Systems -- Computer Sciences); J. Goodenough (Real-Time/Systems
Programming -- SEI); J. McHugh (Secure Systems -- consultant); B. Wichmann
(Safety-Critical Systems -- NPL: UK).

69   This work was regularly reviewed by the Ada 9X Distinguished Reviewers
and the members of the Ada 9X Rapporteur Group (XRG):  E. Ploedereder,
Chairman of DRs and XRG (University of Stuttgart: Germany); B. Bardin
(Hughes); J. Barnes (consultant: UK); B. Brett (DEC); B. Brosgol
(consultant); R. Brukardt (RR Software); N. Cohen (IBM); R. Dewar (NYU);
G. Dismukes (TeleSoft); A. Evans (consultant); A. Gargaro (Computer
Sciences); M. Gerhardt (ESL); J. Goodenough (SEI); S. Heilbrunner (University
of Salzburg: Austria); P. Hilfinger (UC/Berkeley); B. Kaellberg (CelsiusTech:
Sweden); M. Kamrad II (Unisys); J. van Katwijk (Delft University of
Technology: The Netherlands); V. Kaufman (Russia); P. Kruchten (Rational);
R. Landwehr (CCI: Germany); C. Lester (Portsmouth Polytechnic: UK);
L. Mansson (TELIA Research: Sweden); S. Michell (Multiprocessor Toolsmiths:
Canada); M. Mills (US Air Force); D. Pogge (US Navy); K. Power (Boeing);
O. Roubine (Verdix: France); A. Strohmeier (Swiss Fed Inst of Technology:
Switzerland); W. Taylor (consultant: UK); J. Tokar (Tartan); E. Vasilescu
(Grumman); J. Vladik (Prospeks s.r.o.:  Czech Republic); S. Van Vlierberghe
(OFFIS: Belgium).

        69.a   Change:  Various changes at the request of some people
        mentioned above, and Chris Anderson.

70   Other valuable feedback influencing the revision process was provided by
the Ada 9X Language Precision Team (Odyssey Research Associates), the Ada 9X
User/Implementer Teams (AETECH, Tartan, TeleSoft), the Ada 9X Implementation
Analysis Team (New York University) and the Ada community-at-large.

71   Special thanks go to R. Mathis, Convenor of ISO/IEC JTC1/SC22 Working
Group 9.

72   The Ada 9X Project was sponsored by the Ada Joint Program Office.
Christine M. Anderson at the Air Force Phillips Laboratory (Kirtland AFB, NM)
was the project manager.
Changes Since Version 5.0

73   Changes since version 5.0 of 3 June 1994 are marked with change bars.
Thick change bars, like the one next to this paragraph, indicate changes that
might affect an implementation.

74   Thin change bars, like the one next to this paragraph, indicate changes,
such as minor wording changes, that would be unlikely to affect an
implementation.  Change bars are not included in the ASCII version.

75   There are some formatting changes that are not marked.  In addition, we
have made no attempt to mark changes in summary material, such as the Index
or the Informative Annexes; the change bars found in those places are
incomplete.

76   The document submitted to ISO for publication as the International
Standard is the same as this version, except:

   77  This list of ``Changes Since Version 5.0'' is not included in the
       International Standard.

   78  The International Standard does not have change bars.

   79  The list of changes in the Index is not included in the
       International Standard.

   80  The ``Acknowledgements'' page is not included in the
       International Standard.

   81  The text in the running headers and footers on each page is
       slightly different in the International Standard.

   82  The title page(s) are different in the International Standard.

   83  This document is formatted for 8.5-by-11-inch paper, whereas the
       International Standard is formatted for A4 paper (210-by-297mm);
       thus, the page breaks are in different places.

84   Additional formatting changes may be required by ISO before final
publication of the International Standard.

85   These are the changes marked with thick change bars:

   86  An implementation of floating point may support infinities and
       NaNs in Wide_Value, Value, and Get (see 3.5 and A.10.9).

   87  The Wide_Width attribute is added (see 3.5).

   88  An implementation requirement on System.Max_Binary_Modulus was
       added, so at least 16-bit binary modular types have to be
       supported (see 3.5.4).

   89  S'Base'Digits now yields the requested decimal precision of the
       base subtype (see 3.5.7 and 3.5.8).

   90  An abstract subprogram (or primitive function with controlling
       result) need not be overridden for a generic formal tagged
       nonabstract type (see 3.9.3).

   91  A generic formal object of a tagged type is aliased (see 3.10 and
       3.10.2).

   92  An incomplete type is now allowed in an access_to_subprogram_
       definition (see 3.10.1).

   93  The accessibility rules have been rewritten.  The intended effect
       has not changed, but the wording is quite different.  See 3.10.2.
       See also 3.9.1, 4.6, 6.5, 7.6.1, and 9.5.4.  As part of this
       change, the definition of the term ``master'' was slightly
       changed (see 7.6.1, 9.3, 9.8, and 10.2).

   94  The rule about taking 'Access of a discriminant-dependent
       component has been changed to match the corresponding rule for
       renaming.  The rule about P'Access when P is within a generic has
       been changed to refer to the generic body instead of the generic
       unit.  See 3.10.2.

   95  The static expression rules were clarified, and a few bugs were
       fixed (see 4.9).

   96  The rule about multiple access paths has been clarified (see
       6.2).

   97  An inherited subprogram of a generic formal tagged type with
       unknown discriminants is now defined to be intrinsic.  In
       addition, operators defined in language-defined library units may
       be intrinsic.  See 6.3.1.  Ada.Decimal.Divide is also intrinsic
       (see F.2).

   98  The definition of subtype conformance no longer includes a
       special case for convention Intrinsic.  Instead, the special case
       has been moved to the relevant specific rules.  See 6.3.1.  See
       also 3.9.2, 3.10.2, 8.5.4, 12.3, and 13.3.

   99  The definition of full conformance was corrected to include
       character_literals.  The relationship with functional vs.
       operator notation was clarified in the AARM.  See 6.3.1.

  100  The rule about when copy-in is required for composite out
       parameters passed by copy was corrected (see 6.4.1).

  101  The rule about when a full view has to be limited was clarified.
       Some bugs were fixed in the rules about correspondence of
       discriminants between partial and full views.  See 7.3.

  102  Ada.Finalization is now preelaborated (see 7.6).

  103  The Implementation Permission to omit code for (e.g.) ``X := X;''
       was clarified (see 7.6).

  104  Things like ``X: T'Class renames Y;'', where Y is of type T, are
       now illegal (see 8.5.1).  An analogous change was made to generic
       formal objects of mode in out (see 12.4).

  105  The visible part of a task or protected unit includes the
       discriminant part, if any (see 9.1 and 9.4).

  106  The definition of when a task doing an entry call is ``blocked''
       has been clarified (see 9.5.3).

  107  A library unit subprogram renaming declaration is always a
       renaming-as-declaration, never a renaming-as-body (see 10.1.1).

  108  The rules about children of generic packages were changed.  See
       10.1.1.  See also 8.3, 10.1.2, 10.1.6, and 12.2.

  109  An AARM annotation was added clarifying the intent that it is
       illegal for a library subprogram_body with no corresponding
       subprogram_declaration to mention one of its siblings in a with_
       clause if the sibling is a private library unit (see 10.1.2).

  110  Library unit names must be unique (see 10.1.4).

  111  Exception_Name(Constraint_Error'Identity) returns "Constraint_
       Error".  Information is not duplicated among Exception_Name,
       Exception_Message, and Exception_Information.  See 11.4.1.

  112  Legality Rules are re-checked in the formal part of an instance
       (see 12.3).

  113  The rules for discriminant matching in formal private and derived
       types were corrected (see 12.5.1).

  114  Changes were made to the semantics of the Size attribute and
       clause, and some advice that appeared only in Implementation
       Notes in the AARM was moved to Implementation Advice in the RM95
       (see 13.3).

  115  An implementation is allowed (but not required) to declare
       packages System and System.Storage_Elements pure (see 13.7 and
       13.7.1).

  116  Address_To_Access_Conversions is now a library package instead of
       a nested package, and is preelaborated (see 13.7.2).

  117  Unchecked_Conversion is declared pure (see 13.9).

  118  The rules for dereferencing access values designating nonexistent
       objects were corrected (see 13.9.1 and 13.11.2).

  119  Unchecked_Deallocation is preelaborated (see 13.11.2).

  120  The external representation used by 'Write and 'Read has been
       decoupled from the internal representation implied by
       representation items, and the legality rules for representation
       clauses for the stream-related have changed (see 13.13.2 and
       13.3).

  121  Added an AARM annotation clarifying that an implementation may,
       for example, define the Small of type Duration (see A.1).

  122  The package Ada.Characters.Handling is specified with pragma
       Preelaborate, rather than with pragma Pure (see A.3.2).

  123  Wording of the Wide_Character test functions has been revised to
       avoid overspecification of the relationship between Character and
       Wide_Character ranges (see A.3.2).

  124  Names for the control character positions in Characters.Latin_1
       have been corrected (see A.3.3).

  125  The package Strings.Unbounded is specified with pragma
       Preelaborate (see A.4.5).

  126  The package Strings.Maps.Constants is now a child of
       Strings.Maps, and analogously Strings.Wide_Maps.Wide_Constants is
       now a child of Strings.Wide_Maps; the types of the parameters and
       results for several of the Wide_String handling functions have
       been corrected (see A.4.6 and A.4.7).

  127  The Set_Input, Set_Output, and Set_Error procedures that take a
       parameter of type File_Access have been removed from Text_IO (see
       A.10.1).

  128  Input-output for numeric types has been revised with respect to
       the treatment of signs for input with modular types, the
       treatment of signed zeros and other special values for floating
       point input-output, and rounding and accuracy requirements for
       real output (see A.10.8 and A.10.9).

  129  The effect of enumeration output for a character type has been
       clarified (see A.10.10).

  130  Preinstantiations of the numeric IO packages are provided for the
       predefined numeric types (see A.10.8, A.10.9, and A.11).

  131  Added the package Wide_Text_IO.Text_Streams (see A.12.3).

  132  Renamed items in package Command_Line (see A.15).

  133  An AARM-only annotation has been added advising the
       implementation on the names to choose for IEEE floating point
       types (see B.2).

  134  The packages Interfaces.C, Interfaces.C.Strings, and
       Interfaces.C.Pointers include several small enhancements (see
       B.3, B.3.1, and B.3.2).

  135  Corrected a parameter type in Decimal_Conversions (see B.4).

  136  The semantics of pragma Discard_Names has been corrected (see
       C.5).

  137  Implementation permissions related to blocking have been added to
       D.2.1 and D.2.2.

  138  The restrictions on remote types library units now apply only to
       the declaration and not to the body.  Remote access types may now
       be declared in remote types packages.  See Annex E.

  139  The implementation model in the AARM for remote procedure calls
       has been clarified (see E.4).

  140  Added a partition id parameter to Establish_RPC_Receiver (see
       E.5).

  141  Added an AARM note on the intent of the support for decimal
       Machine_Radix (see F.1).

  142  Removed incorrect restriction on the form of a picture string
       (see F.3.1).

  143  Removed obsolete declaration from Text_IO.Editing (see F.3.3).

  144  Revised the description of the model-oriented attributes for
       floating point types (see G.2.2).

  145  Revised the treatment of conversion of fixed point multiplication
       and division to an integer result (see G.2.3).

  146  Corrected some bugs in the rules of J.3, ``Reduced Accuracy
       Subtypes''.



    ----------------------
    INTERNATIONAL STANDARD
    ----------------------











Information technology -- Programming
Languages -- Ada --








                             Section 1: General


1   Ada is a programming language designed to support the construction of
long-lived, highly reliable software systems.  The language includes
facilities to define packages of related types, objects, and operations.  The
packages may be parameterized and the types may be extended to support the
construction of libraries of reusable, adaptable software components.  The
operations may be implemented as subprograms using conventional sequential
control structures, or as entries that include synchronization of concurrent
threads of control as part of their invocation.  The language treats
modularity in the physical sense as well, with a facility to support separate
compilation.

2   The language includes a complete facility for the support of real-time,
concurrent programming.  Errors can be signaled as exceptions and handled
explicitly.  The language also covers systems programming; this requires
precise control over the representation of data and access to
system-dependent properties.  Finally, a predefined environment of standard
packages is provided, including facilities for, among others, input-output,
string manipulation, numeric elementary functions, and random number
generation.

        2.a   Discussion:  This Annotated Ada Reference Manual (AARM)
        contains the entire text of the Ada Reference Manual (RM9X), plus
        certain annotations.  The annotations give a more in-depth analysis
        of the language.  They describe the reason for each non-obvious rule,
        and point out interesting ramifications of the rules and interactions
        among the rules (interesting to language lawyers, that is).
        Differences between Ada 83 and Ada 9X are listed.  (The text you are
        reading now is an annotation.)

        2.b   The AARM stresses detailed correctness and uniformity over
        readability and understandability.  We're not trying to make the
        language ``appear'' simple here; on the contrary, we're trying to
        expose hidden complexities, so we can more easily detect language
        bugs.  The RM9X, on the other hand, is intended to be a more readable
        document for programmers.

        2.c   The annotations in the AARM are as follows:

          2.d  Text that is logically redundant is shown [in square
               brackets, like this].  Technically, such text could be
               written as a Note in the RM9X, since it is really a
               theorem that can be proven from the non-redundant rules
               of the language.  We use the square brackets instead when
               it seems to make the RM9X more readable.

          2.e  The rules of the language (and some AARM-only text) are
               categorized, and placed under certain sub-headings that
               indicate the category.  For example, the distinction
               between Name Resolution Rules and Legality Rules is
               particularly important, as explained in 8.6.

          2.f  Text under the following sub-headings appears in both
               documents:

                 2.g  The unlabeled text at the beginning of each clause
                      or subclause,
                 2.h  Syntax,
                 2.i  Name Resolution Rules,
                 2.j  Legality Rules,
                 2.k  Static Semantics,
                 2.l  Post-Compilation Rules,
                 2.m  Dynamic Semantics,
                 2.n  Bounded (Run-Time) Errors,
                 2.o  Erroneous Execution,
                 2.p  Implementation Requirements,
                 2.q  Documentation Requirements,
                 2.r  Metrics,
                 2.s  Implementation Permissions,
                 2.t  Implementation Advice,
                 2.u  NOTES,
                 2.v  Examples.

          2.w  Text under the following sub-headings does not appear in
               the RM9X:

                 2.x  Language Design Principles,
                 2.y  Inconsistencies With Ada 83,
                 2.z  Incompatibilities With Ada 83,
                2.aa  Extensions to Ada 83,
                2.bb  Wording Changes From Ada 83.

         2.cc  The AARM also includes the following kinds of
               annotations.  These do not necessarily annotate the
               immediately preceding rule, although they often do.

        2.dd   Reason:  An explanation of why a certain rule is necessary, or
        why it is worded in a certain way.

        2.ee   Ramification:  An obscure ramification of the rules that is of
        interest only to language lawyers.  (If a ramification of the rules
        is of interest to programmers, then it appears under NOTES.)

        2.ff   Proof:  An informal proof explaining how a given Note or
        [marked-as-redundant] piece of text follows from the other rules of
        the language.

        2.gg   Implementation Note:  A hint about how to implement a feature,
        or a particular potential pitfall that an implementer needs to be
        aware of.

        2.hh   Change:  Changes to the Ada Reference Manual are annotated
        with one of these when more explanation is needed than the comment
        that triggered the change.  Changes are also marked with the database
        number of the comment that triggered the change, like this:
        {95-9999.a} , unless the change is a spelling or grammar correction,
        a correction of Ada syntax in an example, a font change, a change to
        the index or other summary material, or a change that appears only in
        the AARM.  Changes are also marked with change bars, even if there is
        no corresponding comment in the database.  However, changes to the
        index or other summary material are not always marked with change
        bars.

        2.ii   Discussion:  Other annotations not covered by the above.

        2.jj   To be honest:  A rule that is considered logically necessary
        to the definition of the language, but which is so obscure or
        pedantic that only a language lawyer would care.  These are the only
        annotations that could be considered part of the language definition.

        2.kk   Glossary entry:  The text of a Glossary entry -- this text
        will also appear in Annex N, ``Glossary''.

        2.ll   Discussion:  In general, RM9X text appears in the normal font,
        whereas AARM-only text appears in a smaller font.  Notes also appear
        in the smaller font, as recommended by ISO/IEC style guidelines.  Ada
        examples are also usually printed in a smaller font.

        2.mm   If you have trouble finding things, be sure to use the index.
        {italics, like this} Each defined term appears there, and also in
        italics, like this.  Syntactic categories defined in BNF are also
        indexed.

        2.nn   A definition marked ``[distributed]'' is the main definition
        for a term whose complete definition is given in pieces distributed
        throughout the document.  The pieces are marked ``[partial]'' or with
        a phrase explaining what cases the partial definition applies to.



1.1 Scope

1   This International Standard specifies the form and meaning of programs
written in Ada.  Its purpose is to promote the portability of Ada programs to
a variety of data processing systems.



1.1.1 Extent

1   This International Standard specifies:

    2  The form of a program written in Ada;

    3  The effect of translating and executing such a program;

    4  The manner in which program units may be combined to form Ada
       programs;

    5  The language-defined library units that a conforming implemen-
       tation is required to supply;

    6  The permissible variations within the standard, and the manner in
       which they are to be documented;

    7  Those violations of the standard that a conforming implementation
       is required to detect, and the effect of attempting to translate
       or execute a program containing such violations;

    8  Those violations of the standard that a conforming implementation
       is not required to detect.

9   This International Standard does not specify:

   10  The means whereby a program written in Ada is transformed into
       object code executable by a processor;

   11  The means whereby translation or execution of programs is invoked
       and the executing units are controlled;

   12  The size or speed of the object code, or the relative execution
       speed of different language constructs;

   13  The form or contents of any listings produced by implementations;
       in particular, the form or contents of error or warning messages;

   14  The effect of unspecified execution.

   15  The size of a program or program unit that will exceed the
       capacity of a particular conforming implementation.



1.1.2 Structure

1   This International Standard contains thirteen sections, fourteen annexes,
and an index.

2   {core language} The core of the Ada language consists of:

    3  Sections 1 through 13

    4  Annex A, ``Predefined Language Environment''

    5  Annex B, ``Interface to Other Languages''

    6  Annex J, ``Obsolescent Features''

7   {Specialized Needs Annexes} {Annex (Specialized Needs)} {application
areas} The following Specialized Needs Annexes define features that are
needed by certain application areas:

    8  Annex C, ``Systems Programming''

    9  Annex D, ``Real-Time Systems''

   10  Annex E, ``Distributed Systems''

   11  Annex F, ``Information Systems''

   12  Annex G, ``Numerics''

   13  Annex H, ``Safety and Security''

14   {normative} {Annex (normative)} The core language and the Specialized
Needs Annexes are normative, except that the material in each of the items
listed below is informative:

   15  Text under a NOTES or Examples heading.

   16  Each clause or subclause whose title starts with the word
       ``Example'' or ``Examples''.

17   All implementations shall conform to the core language.  In addition, an
implementation may conform separately to one or more Specialized Needs
Annexes.

18   {informative} {non-normative: see informative} {Annex (informative)} The
following Annexes are informative:

   19  Annex K, ``Language-Defined Attributes''

   20  Annex L, ``Language-Defined Pragmas''

   21  Annex M, ``Implementation-Defined Characteristics''

   22  Annex N, ``Glossary''

   23  Annex P, ``Syntax Summary''

        23.a   Discussion:  The idea of the Specialized Needs Annexes is that
        implementations can choose to target certain application areas.  For
        example, an implementation specifically targeted to embedded machines
        might support the application-specific features for Real-time
        Systems, but not the application-specific features for Information
        Systems.

        23.b   The Specialized Needs Annexes extend the core language only in
        ways that users, implementations, and standards bodies are allowed to
        extend the language; for example, via additional library units,
        attributes, representation items (see 13.1), pragmas, and constraints
        on semantic details that are left unspecified by the core language.
        Many implementations already provide much of the functionality
        defined by Specialized Needs Annexes; our goal is to increase
        uniformity among implementations by defining standard ways of
        providing the functionality.

        23.c   We recommend that the validation procedures allow implemen-
        tations to validate the core language, plus any set of the
        Specialized Needs Annexes.  We recommend that implementations not be
        allowed to validate a portion of one of the Specialized Needs
        Annexes, although implementations can, of course, provide unvalidated
        support for such portions.  We have designed the Specialized Needs
        Annexes assuming that this recommendation is followed.  Thus, our
        decisions about what to include and what not to include in those
        annexes are based on the assumption that each annex is validated in
        an ``all-or-nothing'' manner.

        23.d   An implementation may, of course, support extensions that are
        different from (but possibly related to) those defined by one of the
        Specialized Needs Annexes.  We recommend that, where appropriate,
        implementations do this by adding library units that are children of
        existing language-defined library packages.

        23.e   An implementation should not provide extensions that conflict
        with those defined in the Specialized Needs Annexes, in the following
        sense:  Suppose an implementation supports a certain error-free
        program that uses only functionality defined in the core and in the
        Specialized Needs Annexes.  The implementation should ensure that
        that program will still be error free in some possible full
        implementation of all of the Specialized Needs Annexes, and that the
        semantics of the program will not change.  For example, an
        implementation should not provide a package with the same name as one
        defined in one of the Specialized Needs Annexes, but that behaves
        differently, even if that implementation does not claim conformance
        to that Annex.

        23.f   Note that the Specialized Needs Annexes do not conflict with
        each other; it is the intent that a single implementation can conform
        to all of them.

24   Each section is divided into clauses and subclauses that have a common
structure.  Each section, clause, and subclause first introduces its subject.
After the introductory text, text is labeled with the following headings:


                         Language Design Principles

        24.a   These are not rules of the language, but guiding principles or
        goals used in defining the rules of the language.  In some cases, the
        goal is only partially met; such cases are explained.

        24.b   This is not part of the definition of the language, and does
        not appear in the RM9X.
                                   Syntax

    25   {syntax (under Syntax heading)} {grammar (under Syntax heading)}
    {context free grammar (under Syntax heading)} {BNF (Backus-Naur Form)
    (under Syntax heading)} {Backus-Naur Form (BNF) (under Syntax heading)}
    Syntax rules (indented).


                            Name Resolution Rules

26   {name resolution rules} {overloading rules} {resolution rules}
Compile-time rules that are used in name resolution, including overload
resolution.

        26.a   Discussion:  These rules are observed at compile time.  (We
        say ``observed'' rather than ``checked,'' because these rules are not
        individually checked.  They are really just part of the Legality
        Rules in Section 8 that require exactly one interpretation of each
        constituent of a complete context.)  The only rules used in overload
        resolution are the Syntax Rules and the Name Resolution Rules.

        26.b   When dealing with non-overloadable declarations it sometimes
        makes no semantic difference whether a given rule is a Name
        Resolution Rule or a Legality Rule, and it is sometimes difficult to
        decide which it should be.  We generally make a given rule a Name
        Resolution Rule only if it has to be.  For example, ``The name, if
        any, in a raise_statement shall be the name of an exception.''  is
        under ``Legality Rules.''


                               Legality Rules

27   {legality rules} {compile-time error} {error (compile-time)} Rules that
are enforced at compile time.  {legal (construct)} {illegal (construct)} A
construct is legal if it obeys all of the Legality Rules.

        27.a   Discussion:  These rules are not used in overload resolution.

        27.b   Note that run-time errors are always attached to exceptions;
        for example, it is not ``illegal'' to divide by zero, it just raises
        an exception.


                              Static Semantics

28   {static semantics} {compile-time semantics} A definition of the
compile-time effect of each construct.

        28.a   Discussion:  The most important compile-time effects represent
        the effects on the symbol table associated with declarations
        (implicit or explicit).  In addition, we use this heading as a bit of
        a grab bag for equivalences, package specifications, etc.  For
        example, this is where we put statements like so-and-so is equivalent
        to such-and-such.  (We ought to try to really mean it when we say
        such things!)  Similarly, statements about magically-generated
        implicit declarations go here.  These rules are generally written as
        statements of fact about the semantics, rather than as a
        you-shall-do-such-and-such sort of thing.


                           Post-Compilation Rules

29   {post-compilation rules} {post-compilation error} {post-compilation
rules} {link-time error: see post-compilation error} {error (link-time)}
Rules that are enforced before running a partition.  {legal (partition)}
{illegal (partition)} A partition is legal if its compilation units are legal
and it obeys all of the Post-Compilation Rules.

        29.a   Discussion:  It is not specified exactly when these rules are
        checked, so long as they are checked for any given partition before
        that partition starts running.  An implementation may choose to check
        some such rules at compile time, and reject compilation_units
        accordingly.  Alternatively, an implementation may check such rules
        when the partition is created (usually known as ``link time''), or
        when the partition is mapped to a particular piece of hardware (but
        before the partition starts running).


                              Dynamic Semantics

30   {dynamic semantics} {run-time semantics} {run-time error} {error
(run-time)} A definition of the run-time effect of each construct.

        30.a   Discussion:  This heading describes what happens at run time.
        Run-time checks, which raise exceptions upon failure, are described
        here.  Each item that involves a run-time check is marked with the
        name of the check -- these are the same check names that are used in
        a pragma Suppress.  Principle: Every check should have a name, usable
        in a pragma Suppress.


                          Bounded (Run-Time) Errors

31   {bounded error} {bounded error} Situations that result in bounded
(run-time) errors (see 1.1.5).

        31.a   Discussion:  The ``bounds'' of each such error are described
        here -- that is, we characterize the set of all possible behaviors
        that can result from a bounded error occurring at run time.


                             Erroneous Execution

32   {erroneous execution} {erroneous execution} Situations that result in
erroneous execution (see 1.1.5).


                         Implementation Requirements

33   {implementation requirements} Additional requirements for conforming
implementations.

        33.a   Discussion:  ...as opposed to rules imposed on the programmer.
        An example might be, ``The smallest representable duration,
        Duration'Small, shall not be greater than twenty milliseconds.''

        33.b   It's really just an issue of how the rule is worded.  We could
        write the same rule as ``The smallest representable duration is an
        implementation-defined value less than or equal to 20 milliseconds''
        and then it would be under ``Static Semantics.''


                         Documentation Requirements

34   {documentation requirements} {documentation requirements} Documentation
requirements for conforming implementations.

        34.a   Discussion:  These requirements are beyond those that are
        implicitly specified by the phrase ``implementation defined''.  The
        latter require documentation as well, but we don't repeat these cases
        under this heading.  Usually this heading is used for when the
        description of the documentation requirement is longer and does not
        correspond directly to one, narrow normative sentence.


                                   Metrics

35   {metrics} {metrics} Metrics that are specified for the time/space
properties of the execution of certain language constructs.


                         Implementation Permissions

36   {implementation permissions} Additional permissions given to the
implementer.

        36.a   Discussion:  For example, ``The implementation is allowed to
        impose further restrictions on the record aggregates allowed in code
        statements.''  When there are restrictions on the permission, those
        restrictions are given here also.  For example, ``An implementation
        is allowed to restrict the kinds of subprograms that are allowed to
        be main subprograms.  However, it shall support at least
        parameterless procedures.''  -- we don't split this up between here
        and ``Implementation Requirements.''


                            Implementation Advice

37   {implementation advice} {advice} Optional advice given to the
implementer.  The word ``should'' is used to indicate that the advice is a
recommendation, not a requirement.  It is implementation defined whether or
not a given recommendation is obeyed.

        37.a   Implementation defined:  Whether or not each recommendation
        given in Implementation Advice is followed.

        37.b   Discussion:  The advice generally shows the intended
        implementation, but the implementer is free to ignore it.  The
        implementer is the sole arbiter of whether or not the advice has been
        obeyed, if not, whether the reason is a good one, and whether the
        required documentation is sufficient.  {ACVC [Ada Compiler Validation
        Capability]} {Ada Compiler Validation Capability [ACVC]} It would be
        wrong for the ACVC to enforce any of this advice.

        37.c   For example, ``Whenever possible, the implementation should
        choose a value no greater than fifty microseconds for the smallest
        representable duration, Duration'Small.''

        37.d   We use this heading, for example, when the rule is so low
        level or implementation-oriented as to be untestable.  We also use
        this heading when we wish to encourage implementations to behave in a
        certain way in most cases, but we do not wish to burden
        implementations by requiring the behavior.


     NOTES
38   (1) {notes} Notes emphasize consequences of the rules described in the
     (sub)clause or elsewhere.  This material is informative.


                                  Examples

39   Examples illustrate the possible forms of the constructs described.
This material is informative.

        39.a   Discussion:


        The next three headings list all language changes between Ada 83 and
        Ada 9X.  Language changes are any change that changes the set of text
        strings that are legal Ada programs, or changes the meaning of any
        legal program.  Wording changes, such as changes in terminology, are
        not language changes.  Each language change falls into one of the
        following three categories:


                         Inconsistencies With Ada 83

        39.b   {inconsistencies with Ada 83} {inconsistencies with Ada 83}
        This heading lists all of the upward inconsistencies between Ada 83
        and Ada 9X.  Upward inconsistencies are situations in which a legal
        Ada 83 program is a legal Ada 9X program with different semantics.
        This type of upward incompatibility is the worst type for users, so
        we only tolerate it in rare situations.

        39.c   (Note that the semantics of a program is not the same thing as
        the behavior of the program.  Because of Ada's indeterminacy, the
        ``semantics'' of a given feature describes a set of behaviors that
        can be exhibited by that feature.  The set can contain more than one
        allowed behavior.  Thus, when we ask whether the semantics changes,
        we are asking whether the set of behaviors changes.)

        39.d   This is not part of the definition of the language, and does
        not appear in the RM9X.

                        Incompatibilities With Ada 83

        39.e   {incompatibilities with Ada 83} {incompatibilities with Ada
        83} This heading lists all of the upward incompatibilities between
        Ada 83 and Ada 9X, except for the ones listed under ``Inconsistencies
        With Ada 83'' above.  These are the situations in which a legal Ada
        83 program is illegal in Ada 9X.  We do not generally consider a
        change that turns erroneous execution into an exception, or into an
        illegality, to be upwardly incompatible.

        39.f   This is not part of the definition of the language, and does
        not appear in the RM9X.

                            Extensions to Ada 83

        39.g   {extensions to Ada 83} {extensions to Ada 83} This heading is
        used to list all upward compatible language changes; that is,
        language extensions.  These are the situations in which a legal Ada
        9X program is not a legal Ada 83 program.  The vast majority of
        language changes fall into this category.

        39.h   This is not part of the definition of the language, and does
        not appear in the RM9X.



        39.i   As explained above, the next heading does not represent any
        language change:

                         Wording Changes From Ada 83

        39.j   {wording changes from Ada 83} This heading lists some of the
        non-semantic changes between RM83 and the RM9X.  It is incomplete; we
        have not attempted to list all wording changes, but only the
        ``interesting'' ones.

        39.k   This is not part of the definition of the language, and does
        not appear in the RM9X.



1.1.3 Conformity of an Implementation with the Standard

                         Implementation Requirements

1   {conformance (of an implementation with the Standard)} A conforming
implementation shall:

        1.a   Discussion:  {implementation} The implementation is the
        software and hardware that implements the language.  This includes
        compiler, linker, operating system, hardware, etc.

        1.b   We first define what it means to ``conform'' in general --
        basically, the implementation has to properly implement the normative
        rules given throughout the standard.  Then we define what it means to
        conform to a Specialized Needs Annex -- the implementation must
        support the core features plus the features of that Annex.  Finally,
        we define what it means to ``conform to the Standard'' -- this
        requires support for the core language, and allows partial (but not
        conflicting) support for the Specialized Needs Annexes.

    2  Translate and correctly execute legal programs written in Ada,
       provided that they are not so large as to exceed the capacity of
       the implementation;

    3  Identify all programs or program units that are so large as to
       exceed the capacity of the implementation (or raise an
       appropriate exception at run time);

 3.a    Implementation defined:  Capacity limitations of the
        implementation.

    4  Identify all programs or program units that contain errors whose
       detection is required by this International Standard;

 4.a    Discussion:  Note that we no longer use the term ``rejection''
        of programs or program units.  We require that programs or
        program units with errors or that exceed some capacity limit be
        ``identified.''  The way in which errors or capacity problems
        are reported is not specified.

 4.b    An implementation is allowed to use standard error-recovery
        techniques.  We do not disallow such techniques from being used
        across compilation_unit or compilation boundaries.

 4.c    See also the Implementation Requirements of 10.2, which disallow
        the execution of illegal partitions.  {94-4712.a}

    5  Supply all language-defined library units required by this
       International Standard;

 5.a    Implementation Note:  An implementation cannot add to or modify
        the visible part of a language-defined library unit, except
        where such permission is explicitly granted, unless such
        modifications are semantically neutral with respect to the
        client compilation units of the library unit.  An implementation
        defines the contents of the private part and body of
        language-defined library units.

 5.b    An implementation can add with_clauses and use_clauses, since
        these modifications are semantically neutral to clients.  (The
        implementation might need with_clauses in order to implement the
        private part, for example.)  Similarly, an implementation can
        add a private part even in cases where a private part is not
        shown in the standard.  Explicit declarations can be provided
        implicitly or by renaming, provided the changes are semantically
        neutral.

 5.c    {italics (implementation-defined)} Wherever in the standard the
        text of a language-defined library unit contains an italicized
        phrase starting with ``implementation-defined'', the
        implementation's version will replace that phrase with some
        implementation-defined text that is syntactically legal at that
        place, and follows any other applicable rules.

 5.d    Note that modifications are permitted, even if there are other
        tools in the environment that can detect the changes (such as a
        program library browser), so long as the modifications make no
        difference with respect to the static or dynamic semantics of
        the resulting programs, as defined by the standard.

    6  Contain no variations except those explicitly permitted by this
       International Standard, or those that are impossible or
       impractical to avoid given the implementation's execution
       environment;

 6.a    Implementation defined:  Variations from the standard that are
        impractical to avoid given the implementation's execution
        environment.

 6.b    Reason:  The ``impossible or impractical'' wording comes from
        AI-325.  It takes some judgement and common sense to interpret
        this.  Restricting compilation units to less than 4 lines is
        probably unreasonable, whereas restricting them to less than 4
        billion lines is probably reasonable (at least given today's
        technology).  We do not know exactly where to draw the line, so
        we have to make the rule vague.

    7  Specify all such variations in the manner prescribed by this
       International Standard.  {94-4485.d} {94-4749.a}

8   {external effect (of the execution of an Ada program)} {effect
(external)} The external effect of the execution of an Ada program is defined
in terms of its interactions with its external environment.  {external
interaction} The following are defined as external interactions:

    9  Any interaction with an external file (see A.7);

   10  The execution of certain code_statements (see 13.8); which code_
       statements cause external interactions is implementation defined.

 10.a   Implementation defined:  Which code_statements cause external
        interactions.

   11  Any call on an imported subprogram (see Annex B), including any
       parameters passed to it;

   12  Any result returned or exception propagated from a main
       subprogram (see 10.2) or an exported subprogram (see Annex B) to
       an external caller;

 12.a   Discussion:  By ``result returned'' we mean to include function
        results and values returned in [in] out parameters.

   13  [Any read or update of an atomic or volatile object (see C.6);]

   14  The values of imported and exported objects (see Annex B) at the
       time of any other interaction with the external environment.

 14.a   To be honest:  Also other uses of imported and exported
        entities, as defined by the implementation, if the
        implementation supports such pragmas.

15   A conforming implementation of this International Standard shall produce
for the execution of a given Ada program a set of interactions with the
external environment whose order and timing are consistent with the
definitions and requirements of this International Standard for the semantics
of the given program.

        15.a   Ramification:  There is no need to produce any of the
        ``internal effects'' defined for the semantics of the program -- all
        of these can be optimized away -- so long as an appropriate sequence
        of external interactions is produced.

        15.b   Discussion:  See also 11.6 which specifies various liberties
        associated with optimizations in the presence of language-defined
        checks, that could change the external effects that might be
        produced.  These alternative external effects are still consistent
        with the standard, since 11.6 is part of the standard.

        15.c   Note also that we only require ``an appropriate sequence of
        external interactions'' rather than ``the same sequence...''  An
        optimizer may cause a different sequence of external interactions to
        be produced than would be produced without the optimizer, so long as
        the new sequence still satisfies the requirements of the standard.
        For example, optimization might affect the relative rate of progress
        of two concurrent tasks, thereby altering the order in which two
        external interactions occur.

        15.d   Note that RM83 explicitly mentions the case of an ``exact
        effect'' of a program, but since so few programs have their effects
        defined that exactly, we don't even mention this ``special'' case.
        In particular, almost any program that uses floating point or tasking
        has to have some level of inexactness in the specification of its
        effects.  And if one includes aspects of the timing of the external
        interactions in the external effect of the program (as is appropriate
        for a real-time language), no ``exact effect'' can be specified.  For
        example, if two external interactions initiated by a single task are
        separated by a ``delay 1.0;'' then the language rules imply that the
        two external interactions have to be separated in time by at least
        one second, as defined by the clock associated with the delay_
        relative_statement.  This in turn implies that the time at which an
        external interaction occurs is part of the characterization of the
        external interaction, at least in some cases, again making the
        specification of the required ``exact effect'' impractical.

16   An implementation that conforms to this Standard shall support each
capability required by the core language as specified.  In addition, an
implementation that conforms to this Standard may conform to one or more
Specialized Needs Annexes (or to none).  Conformance to a Specialized Needs
Annex means that each capability required by the Annex is provided as
specified.

        16.a   Discussion:  The last sentence defines what it means to say
        that an implementation conforms to a Specialized Needs Annex, namely,
        only by supporting all capabilities required by the Annex.

17   An implementation conforming to this International Standard may provide
additional attributes, library units, and pragmas.  However, it shall not
provide any attribute, library unit, or pragma having the same name as an
attribute, library unit, or pragma (respectively) specified in a Specialized
Needs Annex unless the provided construct is either as specified in the
Specialized Needs Annex or is more limited in capability than that required
by the Annex.  A program that attempts to use an unsupported capability of an
Annex shall either be identified by the implementation before run time or
shall raise an exception at run time.

        17.a   Discussion:  The last sentence of the preceding paragraph
        defines what an implementation is allowed to do when it does not
        "conform" to a Specialized Needs Annex.  In particular, the sentence
        forbids implementations from providing a construct with the same name
        as a corresponding construct in a Specialized Needs Annex but with a
        different syntax (e.g., an extended syntax) or quite different
        semantics.  The phrase concerning "more limited in capability" is
        intended to give permission to provide a partial implementation, such
        as not implementing a subprogram in a package or having a restriction
        not permitted by an implementation that conforms to the Annex.  For
        example, a partial implementation of the package Ada.Decimal might
        have Decimal.Max_Decimal_Digits as 15 (rather than the required 18).
        This allows a partial implementation to grow to a fully conforming
        implementation.

        17.b   A restricted implementation might be restricted by not
        providing some subprograms specified in one of the packages defined
        by an Annex.  In this case, a program that tries to use the missing
        subprogram will usually fail to compile.  Alternatively, the
        implementation might declare the subprogram as abstract, so it cannot
        be called.  {Program_Error (raised by failure of run-time check)}
        Alternatively, a subprogram body might be implemented just to raise
        Program_Error.  The advantage of this approach is that a program to
        be run under a fully conforming Annex implementation can be checked
        syntactically and semantically under an implementation that only
        partially supports the Annex.  Finally, an implementation might
        provide a package declaration without the corresponding body, so that
        programs can be compiled, but partitions cannot be built and
        executed.

        17.c   To ensure against wrong answers being delivered by a partial
        implementation, implementers are required to raise an exception when
        a program attempts to use an unsupported capability and this can be
        detected only at run time.  For example, a partial implementation of
        Ada.Decimal might require the length of the Currency string to be 1,
        and hence, an exception would be raised if a subprogram were called
        in the package Edited_Output with a length greater than 1.


                         Documentation Requirements

18   {documentation requirements} {implementation defined} {unspecified}
{specified (not!)} {implementation-dependent: see unspecified} {documentation
(required of an implementation)} Certain aspects of the semantics are defined
to be either implementation defined or unspecified.  In such cases, the set
of possible effects is specified, and the implementation may choose any
effect in the set.  Implementations shall document their behavior in
implementation-defined situations, but documentation is not required for
unspecified situations.  The implementation-defined characteristics are
summarized in Annex M.

        18.a   Discussion:  We used to use the term ``implementation
        dependent'' instead of ``unspecified''.  However, that sounded too
        much like ``implementation defined''.  Furthermore, the term
        ``unspecified'' is used in the ANSI C and POSIX standards for this
        purpose, so that is another advantage.  We also use ``not specified''
        and ``not specified by the language'' as synonyms for
        ``unspecified.''  The documentation requirement is the only
        difference between implementation defined and unspecified.

        18.b   Note that the ``set of possible effects'' can be ``all
        imaginable effects'', as is the case with erroneous execution.

19   The implementation may choose to document implementation-defined
behavior either by documenting what happens in general, or by providing some
mechanism for the user to determine what happens in a particular case.

        19.a   Discussion:  For example, if the standard says that library
        unit elaboration order is implementation defined, the implementation
        might describe (in its user's manual) the algorithm it uses to
        determine the elaboration order.  On the other hand, the
        implementation might provide a command that produces a description of
        the elaboration order for a partition upon request from the user.  It
        is also acceptable to provide cross references to existing
        documentation (for example, a hardware manual), where appropriate.

        19.b   Note that dependence of a program on implementation-defined or
        unspecified functionality is not defined to be an error; it might
        cause the program to be less portable, however.


                            Implementation Advice

20   {Program_Error (raised by failure of run-time check)} If an
implementation detects the use of an unsupported Specialized Needs Annex
feature at run time, it should raise Program_Error if feasible.

        20.a   Reason:  The reason we don't require Program_Error is that
        there are situations where other exceptions might make sense.  For
        example, if the Real Time Systems Annex requires that the range of
        System.Priority include at least 30 values, an implementation could
        conform to the Standard (but not to the Annex) if it supported only
        12 values.  Since the rules of the language require Constraint_Error
        to be raised for out-of-range values, we cannot require Program_Error
        to be raised instead.

21   If an implementation wishes to provide implementation-defined extensions
to the functionality of a language-defined library unit, it should normally
do so by adding children to the library unit.

        21.a   Implementation Note:  If an implementation has support code
        (``run-time system code'') that is needed for the execution of
        user-defined code, it can put that support code in child packages of
        System.  Otherwise, it has to use some trick to avoid polluting the
        user's namespace.  It is important that such tricks not be available
        to user-defined code (not in the standard mode, at least) -- that
        would defeat the purpose.


     NOTES
22   (2) The above requirements imply that an implementation conforming to
     this Standard may support some of the capabilities required by a
     Specialized Needs Annex without supporting all required capabilities.

   22.a   Discussion:  A conforming implementation can partially support a
        Specialized Needs Annex.  Such an implementation does not conform to
        the Annex, but it does conform to the Standard.



1.1.4 Method of Description and Syntax Notation

1   The form of an Ada program is described by means of a context-free syntax
together with context-dependent requirements expressed by narrative rules.

2   The meaning of Ada programs is described by means of narrative rules
defining both the effects of each construct and the composition rules for
constructs.

3   {syntax (notation)} {grammar (notation)} {context free grammar
(notation)} {BNF (Backus-Naur Form) (notation)} {Backus-Naur Form (BNF)
(notation)} The context-free syntax of the language is described using a
simple variant of Backus-Naur Form.  In particular:

    4  Lower case words in a sans-serif font, some containing embedded
       underlines, are used to denote syntactic categories, for example:

5          case_statement

    6  Boldface words are used to denote reserved words, for example:

7          array

    8  Square brackets enclose optional items.  Thus the two following
       rules are equivalent.

9          return_statement ::= return [expression];
           return_statement ::= return; | return expression;

   10  Curly brackets enclose a repeated item.  The item may appear zero
       or more times; the repetitions occur from left to right as with
       an equivalent left-recursive rule.  Thus the two following rules
       are equivalent.

11         term ::= factor {multiplying_operator factor}
           term ::= factor | term multiplying_operator factor

   12  A vertical line separates alternative items unless it occurs
       immediately after an opening curly bracket, in which case it
       stands for itself:

13         constraint ::= scalar_constraint | composite_constraint
           discrete_choice_list ::= discrete_choice {| discrete_choice}

   14  {italics (syntax rules)} If the name of any syntactic category
       starts with an italicized part, it is equivalent to the category
       name without the italicized part.  The italicized part is
       intended to convey some semantic information.  For example
       subtype_name and task_name are both equivalent to name alone.

        14.a   Discussion:  {LR(1)} {ambiguous grammar} {grammar (resolution
        of ambiguity)} {grammar (ambiguous)} The grammar given in the RM9X is
        not LR(1).  In fact, it is ambiguous; the ambiguities are resolved by
        the overload resolution rules (see 8.6).

        14.b   We often use ``if'' to mean ``if and only if'' in definitions.
        For example, if we define ``photogenic'' by saying, ``A type is
        photogenic if it has the following properties...,'' we mean that a
        type is photogenic if and only if it has those properties.  It is
        usually clear from the context, and adding the ``and only if'' seems
        too cumbersome.

        14.c   When we say, for example, ``a declarative_item of a
        declarative_part'', we are talking about a declarative_item
        immediately within that declarative_part.  When we say ``a
        declarative_item in, or within, a declarative_part'', we are talking
        about a declarative_item anywhere in the declarative_part, possibly
        deeply nested within other declarative_parts.  (This notation doesn't
        work very well for names, since the name ``of'' something also has
        another meaning.)

        14.d   When we refer to the name of a language-defined entity (for
        example, Duration), we mean the language-defined entity even in
        programs where the declaration of the language-defined entity is
        hidden by another declaration.  For example, when we say that the
        expected type for the expression of a delay_relative_statement is
        Duration, we mean the language-defined type Duration that is declared
        in Standard, not some type Duration the user might have declared.

15   {syntactic category} A syntactic category is a nonterminal in the
grammar defined in BNF under ``Syntax.''  Names of syntactic categories are
set in a different font, like_this.

16   {Construct} [glossary entry]A construct is a piece of text (explicit or
implicit) that is an instance of a syntactic category defined under
``Syntax.''

        16.a   Ramification:  For example, an expression is a construct.  A
        declaration is a construct, whereas the thing declared by a
        declaration is an ``entity.''

        16.b   Discussion:  ``Explicit'' and ``implicit'' don't mean exactly
        what you might think they mean:  The text of an instance of a generic
        is considered explicit, even though it does not appear explicitly (in
        the non-technical sense) in the program text, and even though its
        meaning is not defined entirely in terms of that text.

17   {constituent (of a construct)} A constituent of a construct is the
construct itself, or any construct appearing within it.

18   {arbitrary order} Whenever the run-time semantics defines certain
actions to happen in an arbitrary order, this means that the implementation
shall arrange for these actions to occur in a way that is equivalent to some
sequential order, following the rules that result from that sequential order.
When evaluations are defined to happen in an arbitrary order, with conversion
of the results to some subtypes, or with some run-time checks, the
evaluations, conversions, and checks may be arbitrarily interspersed, so long
as each expression is evaluated before converting or checking its value.
{type conversion [arbitrary order]} {conversion [arbitrary order]} [Note that
the effect of a program can depend on the order chosen by the implementation.
This can happen, for example, if two actual parameters of a given call have
side effects.]

        18.a   Discussion:  Programs will be more portable if their external
        effect does not depend on the particular order chosen by an
        implementation.

        18.b   Ramification:  Additional reordering permissions are given in
        11.6, ``Exceptions and Optimization''.

        18.c   There is no requirement that the implementation always choose
        the same order in a given kind of situation.  In fact, the
        implementation is allowed to choose a different order for two
        different executions of the same construct.  However, we expect most
        implementations will behave in a relatively predictable manner in
        most situations.

        18.d   Reason:  The ``sequential order'' wording is intended to allow
        the programmer to rely on ``benign'' side effects.  For example, if F
        is a function that returns a unique integer by incrementing some
        global and returning the result, a call such as P(F, F) is OK if the
        programmer cares only that the two results of F are unique; the two
        calls of F cannot be executed in parallel, unless the compiler can
        prove that parallel execution is equivalent to some sequential order.


     NOTES
19   (3) The syntax rules describing structured constructs are presented in a
     form that corresponds to the recommended paragraphing.  For example, an
     if_statement is defined as:

20       if_statement ::=
             if condition then
               sequence_of_statements
            {elsif condition then
               sequence_of_statements}
            [else
               sequence_of_statements]
             end if;

21   (4) The line breaks and indentation in the syntax rules indicate the
     recommended line breaks and indentation in the corresponding constructs.
     The preferred places for other line breaks are after semicolons.



1.1.5 Classification of Errors

                         Implementation Requirements

1   The language definition classifies errors into several different
categories:

    2   Errors that are required to be detected prior to run time by
       every Ada implementation;

       3   These errors correspond to any violation of a rule given in
       this International Standard, other than those listed below.  In
       particular, violation of any rule that uses the terms shall,
       allowed, permitted, legal, or illegal belongs to this category.
       Any program that contains such an error is not a legal Ada
       program; on the other hand, the fact that a program is legal does
       not mean, per se, that the program is free from other forms of
       error.

       4   {compile-time error} {error (compile-time)} {link-time error:
       see post-compilation error} {error (link-time)} The rules are
       further classified as either compile time rules, or post
       compilation rules, depending on whether a violation has to be
       detected at the time a compilation unit is submitted to the
       compiler, or may be postponed until the time a compilation unit
       is incorporated into a partition of a program.

        4.a   Ramification:  See, for example, 10.1.3, ``Subunits of
        Compilation Units'', for some errors that are detected only
        after compilation.  Implementations are allowed, but not
        required, to detect post compilation rules at compile time when
        possible.

    5   Errors that are required to be detected at run time by the
       execution of an Ada program;

       6   {run-time error} {error (run-time)} The corresponding error
       situations are associated with the names of the predefined
       exceptions.  Every Ada compiler is required to generate code that
       raises the corresponding exception if such an error situation
       arises during program execution.  [If such an error situation is
       certain to arise in every execution of a construct, then an
       implementation is allowed (although not required) to report this
       fact at compilation time.]  {94-4776.a}

    7   Bounded errors;

       8   The language rules define certain kinds of errors that need
       not be detected either prior to or during run time, but if not
       detected, the range of possible effects shall be bounded.
       {bounded error} The errors of this category are called bounded
       errors.  {Program_Error (raised by failure of run-time check)}
       The possible effects of a given bounded error are specified for
       each such error, but in any case one possible effect of a bounded
       error is the raising of the exception Program_Error.

    9   Erroneous execution.

       10   {erroneous execution} In addition to bounded errors, the
       language rules define certain kinds of errors as leading to
       erroneous execution.  Like bounded errors, the implementation
       need not detect such errors either prior to or during run time.
       Unlike bounded errors, there is no language-specified bound on
       the possible effect of erroneous execution; the effect is in
       general not predictable.

        10.a   Ramification:  Executions are erroneous, not programs or
        parts of programs.  Once something erroneous happens, the
        execution of the entire program is erroneous from that point on,
        and potentially before given possible reorderings permitted by
        11.6 and elsewhere.  We cannot limit it to just one partition,
        since partitions are not required to live in separate address
        spaces.  (But implementations are encouraged to limit it as much
        as possible.)

        10.b   Suppose a program contains a pair of things that will be
        executed ``in an arbitrary order.''  It is possible that one
        order will result in something sensible, whereas the other order
        will result in erroneous execution.  If the implementation
        happens to choose the first order, then the execution is not
        erroneous.  This may seem odd, but it is not harmful.

        10.c   Saying that something is erroneous is semantically
        equivalent to saying that the behavior is unspecified.  However,
        ``erroneous'' has a slightly more disapproving flavor.


                         Implementation Permissions

11   [{mode of operation (nonstandard)} {nonstandard mode} An implementation
may provide nonstandard modes of operation.  Typically these modes would be
selected by a pragma or by a command line switch when the compiler is
invoked.  When operating in a nonstandard mode, the implementation may reject
compilation_units that do not conform to additional requirements associated
with the mode, such as an excessive number of warnings or violation of coding
style guidelines.  Similarly, in a nonstandard mode, the implementation may
apply special optimizations or alternative algorithms that are only
meaningful for programs that satisfy certain criteria specified by the
implementation.  {mode of operation (standard)} {standard mode} In any case,
an implementation shall support a standard mode that conforms to the
requirements of this International Standard; in particular, in the standard
mode, all legal compilation_units shall be accepted.]

        11.a   Discussion:  These permissions are designed to authorize
        explicitly the support for alternative modes.  Of course, nothing we
        say can prevent them anyway, but this (redundant) paragraph is
        designed to indicate that such alternative modes are in some sense
        ``approved'' and even encouraged where they serve the specialized
        needs of a given user community, so long as the standard mode,
        designed to foster maximum portability, is always available.


                            Implementation Advice

12   {Program_Error (raised by failure of run-time check)} If an
implementation detects a bounded error or erroneous execution, it should
raise Program_Error.


                         Wording Changes From Ada 83

        12.a   Some situations that are erroneous in Ada 83 are no longer
        errors at all.  For example, depending on the parameter passing
        mechanism when unspecified is possibly non-portable, but not
        erroneous.

        12.b   Other situations that are erroneous in Ada 83 are changed to
        be bounded errors.  In particular, evaluating an uninitialized scalar
        variable is a bounded error.  {Program_Error (raised by failure of
        run-time check)} The possible results are to raise Program_Error (as
        always), or to produce a machine-representable value (which might not
        be in the subtype of the variable).  {Constraint_Error (raised by
        failure of run-time check)} Violating a Range_Check or Overflow_Check
        raises Constraint_Error, even if the value came from an uninitialized
        variable.  This means that optimizers can no longer ``assume'' that
        all variables are initialized within their subtype's range.
        Violating a check that is suppressed remains erroneous.

        12.c   The ``incorrect order dependences'' category of errors is
        removed.  All such situations are simply considered potential
        non-portabilities.  This category was removed due to the difficulty
        of defining what it means for two executions to have a ``different
        effect.''  For example, if a function with a side-effect is called
        twice in a single expression, it is not in principle possible for the
        compiler to decide whether the correctness of the resulting program
        depends on the order of execution of the two function calls.  A
        compile time warning might be appropriate, but raising of Program_
        Error at run time would not be.



1.2 Normative References

1   {references} {bibliography} The following standards contain provisions
which, through reference in this text, constitute provisions of this
International Standard.  At the time of publication, the editions indicated
were valid.  All standards are subject to revision, and parties to agreements
based on this International Standard are encouraged to investigate the
possibility of applying the most recent editions of the standards indicated
below.  Members of IEC and ISO maintain registers of currently valid
International Standards.

2   {ISO/IEC 646:1991} {646:1991, ISO/IEC standard} {character set standard
(7-bit)} ISO/IEC 646:1991, Information technology -- ISO 7-bit coded
character set for information interchange.

3   {ISO/IEC 1539:1991} {1539:1991, ISO/IEC standard} {FORTRAN standard}
ISO/IEC 1539:1991, Information technology -- Programming languages --
FORTRAN.

4   {ISO 1989:1985} {1989:1985, ISO standard} {COBOL standard} ISO 1989:1985,
Programming languages -- COBOL.

5   {ISO/IEC 6429:1992} {6429:1992, ISO/IEC standard} {character set standard
(control functions)} ISO/IEC 6429:1992, Information technology -- Control
functions for coded graphic character sets.

6   {ISO/IEC 8859-1:1987} {8859-1:1987, ISO/IEC standard} {character set
standard (8-bit)} ISO/IEC 8859-1:1987, Information processing -- 8-bit
single-byte coded character sets -- Part 1: Latin alphabet No. 1.

7   {ISO/IEC 9899:1990} {9899:1990, ISO/IEC standard} {C standard} ISO/IEC
9899:1990, Programming languages -- C.

8   {ISO/IEC 10646-1:1993} {10646-1:1993, ISO/IEC standard} {character set
standard (16-bit)} ISO/IEC 10646-1:1993, Information technology -- Universal
Multiple-Octet Coded Character Set (UCS) -- Part 1: Architecture and Basic
Multilingual Plane.  {94-4485.f}

        8.a   Discussion:  {POSIX} POSIX, Portable Operating System Interface
        (POSIX) -- Part 1: System Application Program Interface (API) [C
        Language], The Institute of Electrical and Electronics Engineers,
        1990.



1.3 Definitions

1   {italics (terms introduced or defined)} Terms are defined throughout this
International Standard, indicated by italic type.  Terms explicitly defined
in this International Standard are not to be presumed to refer implicitly to
similar terms defined elsewhere.  Terms not defined in this International
Standard are to be interpreted according to the Webster's Third New
International Dictionary of the English Language.  Informal descriptions of
some terms are also given in Annex N, ``Glossary''.

        1.a   Discussion:  The index contains an entry for every defined
        term.

        1.b   Glossary entry:  Each term defined in Annex N is marked like
        this.


        1.c   Discussion:  Here are some AARM-only definitions:  {Ada
        Rapporteur Group (ARG)} {ARG} The Ada Rapporteur Group (ARG)
        interprets the RM83.  {Ada Issue (AI)} {AI} An Ada Issue (AI) is a
        numbered ruling from the ARG.  {Ada Commentary Integration Document
        (ACID)} {ACID} The Ada Commentary Integration Document (ACID) is an
        edition of RM83 in which clearly marked insertions and deletions
        indicate the effect of integrating the approved AIs.  {Uniformity
        Rapporteur Group (URG)} {URG} The Uniformity Rapporteur Group (URG)
        issues recommendations intended to increase uniformity across Ada
        implementations.  {Uniformity Issue (UI)} {UI} A Uniformity Issue
        (UI) is a numbered recommendation from the URG.



                         Section 2: Lexical Elements


1   [The text of a program consists of the texts of one or more compilations.
The text of a compilation is a sequence of lexical elements, each composed of
characters; the rules of composition are given in this section.  Pragmas,
which provide certain information for the compiler, are also described in
this section.]



2.1 Character Set

1   {character set} The only characters allowed outside of comments are the
graphic_characters and format_effectors.

        1.a   Ramification:  Any character, including an other_control_
        function, is allowed in a comment.

        1.b   Note that this rule doesn't really have much force, since the
        implementation can represent characters in the source in any way it
        sees fit.  For example, an implementation could simply define that
        what seems to be a non-graphic, non-format-effector character is
        actually a representation of the space character.

        1.c   Discussion:  It is our intent to follow the terminology of ISO
        10646 BMP where appropriate, and to remain compatible with the
        character classifications defined in A.3, ``Character Handling''.
        Note that our definition for graphic_character is more inclusive than
        that of ISO 10646-1.
                                   Syntax

2   character ::= graphic_character | format_effector | other_control_function

3   graphic_character ::= identifier_letter | digit | space_character | special\
_character


                              Static Semantics

4   The character repertoire for the text of an Ada program consists of the
collection of characters called the Basic Multilingual Plane (BMP) of the ISO
10646 Universal Multiple-Octet Coded Character Set, plus a set of format_
effectors and, in comments only, a set of other_control_functions; the coded
representation for these characters is implementation defined [(it need not
be a representation defined within ISO-10646-1)].

        4.a   Implementation defined:  The coded representation for the text
        of an Ada program.

5   The description of the language definition in this International Standard
uses the graphic symbols defined for Row 00: Basic Latin and Row 00: Latin-1
Supplement of the ISO 10646 BMP; these correspond to the graphic symbols of
ISO 8859-1 (Latin-1); no graphic symbols are used in this International
Standard for characters outside of Row 00 of the BMP.  The actual set of
graphic symbols used by an implementation for the visual representation of
the text of an Ada program is not specified.  {unspecified [partial]}

6   The categories of characters are defined as follows:

7   {identifier_letter} identifier_letter
                upper_case_identifier_letter | lower_case_identifier_letter

7.a     Discussion:  We use identifier_letter instead of simply letter
        because ISO 10646 BMP includes many other characters that would
        generally be considered "letters."

8   {upper_case_identifier_letter} upper_case_identifier_letter
                Any character of Row 00 of ISO 10646 BMP whose name begins
                ``Latin Capital Letter''.

9   {lower_case_identifier_letter} lower_case_identifier_letter
                Any character of Row 00 of ISO 10646 BMP whose name begins
                ``Latin Small Letter''.

10  {digit} digit
                One of the characters 0, 1, 2, 3, 4, 5, 6, 7, 8, or 9.

11  {space_character} space_character
                The character of ISO 10646 BMP named ``Space''.

12  {special_character} special_character
                Any character of the ISO 10646 BMP that is not reserved for a
                control function, and is not the space_character, an
                identifier_letter, or a digit.

12.a    Ramification:  Note that the no break space and soft hyphen are
        special_characters, and therefore graphic_characters.  They are not
        the same characters as space and hyphen-minus.

13  {format_effector} format_effector
                The control functions of ISO 6429 called character tabulation
                (HT), line tabulation (VT), carriage return (CR), line feed
                (LF), and form feed (FF).  {control character: see also
                format_effector}

14  {other_control_function} other_control_function
                Any control function, other than a format_effector, that is
                allowed in a comment; the set of other_control_functions
                allowed in comments is implementation defined.

14.a    Implementation defined:  The control functions allowed in comments.

                {control character: see also other_control_function}

15   {names of special_characters} {special_character (names)} The following
names are used when referring to certain special_characters:  {quotation
mark} {number sign} {ampersand} {apostrophe} {tick} {left parenthesis} {right
parenthesis} {asterisk} {multiply} {plus sign} {comma} {hyphen-minus} {minus}
{full stop} {dot} {point} {solidus} {divide} {colon} {semicolon} {less-than
sign} {equals sign} {greater-than sign} {low line} {underline} {vertical
line} {left square bracket} {right square bracket} {left curly bracket}
{right curly bracket}

        15.a   Discussion:  These are the ones that play a special role in
        the syntax of Ada 9X, or in the syntax rules; we don't bother to
        define names for all characters.  The first name given is the name
        from ISO 10646-1; the subsequent names, if any, are those used within
        the standard, depending on context.

    symbol     name                       symbol     name

      "        quotation mark               :        colon
      #        number sign                  ;        semicolon
      &        ampersand                    <        less-than sign
      '        apostrophe, tick             =        equals sign
      (        left parenthesis             >        greater-than sign
      )        right parenthesis            _        low line, underline
      *        asterisk, multiply           |        vertical line
      +        plus sign                    [        left square bracket
      ,        comma                        ]        right square bracket
      -        hyphen-minus, minus          {        left curly bracket
      .        full stop, dot, point        }        right curly bracket
      /        solidus, divide



                         Implementation Permissions

16   In a nonstandard mode, the implementation may support a different
character repertoire[; in particular, the set of characters that are
considered identifier_letters can be extended or changed to conform to local
conventions].

        16.a   Ramification:  If an implementation supports other character
        sets, it defines which characters fall into each category, such as
        ``identifier_letter,'' and what the corresponding rules of this
        section are, such as which characters are allowed in the text of a
        program.


     NOTES
17   (1) Every code position of ISO 10646 BMP that is not reserved for a
     control function is defined to be a graphic_character by this
     International Standard.  This includes all code positions other than
     0000 - 001F, 007F - 009F, and FFFE - FFFF.

18   (2) The language does not specify the source representation of programs.

   18.a   Discussion:  Any source representation is valid so long as the
        implementer can produce an (information-preserving) algorithm for
        translating both directions between the representation and the
        standard character set.  (For example, every character in the
        standard character set has to be representable, even if the output
        devices attached to a given computer cannot print all of those
        characters properly.)  From a practical point of view, every
        implementer will have to provide some way to process the ACVC.  It is
        the intent to allow source representations, such as parse trees, that
        are not even linear sequences of characters.  It is also the intent
        to allow different fonts:  reserved words might be in bold face, and
        that should be irrelevant to the semantics.


                            Extensions to Ada 83

        18.b   {extensions to Ada 83} Ada 9X allows 8-bit and 16-bit
        characters, as well as implementation-specified character sets.

                         Wording Changes From Ada 83

        18.c   The syntax rules in this clause are modified to remove the
        emphasis on basic characters vs. others.  (In this day and age, there
        is no need to point out that you can write programs without using
        (for example) lower case letters.)  In particular, character
        (representing all characters usable outside comments) is added, and
        basic_graphic_character, other_special_character, and basic_character
        are removed.  Special_character is expanded to include Ada 83's
        other_special_character, as well as new 8-bit characters not present
        in Ada 83.  Note that the term ``basic letter'' is used in A.3,
        ``Character Handling'' to refer to letters without diacritical marks.

        18.d   Character names now come from ISO 10646.

        18.e   We use identifier_letter rather than letter since ISO 10646
        BMP includes many "letters' that are not permitted in identifiers (in
        the standard mode).



2.2 Lexical Elements, Separators, and Delimiters

                              Static Semantics

1   {text of a program} The text of a program consists of the texts of one or
more compilations.  {lexical element} {token: see lexical element} The text
of each compilation is a sequence of separate lexical elements.  Each lexical
element is formed from a sequence of characters, and is either a delimiter,
an identifier, a reserved word, a numeric_literal, a character_literal, a
string_literal, or a comment.  The meaning of a program depends only on the
particular sequences of lexical elements that form its compilations,
excluding comments.

2   The text of a compilation is divided into {line} lines.  {end of a line}
In general, the representation for an end of line is implementation defined.

        2.a   Implementation defined:  The representation for an end of line.

However, a sequence of one or more format_effectors other than character
tabulation (HT) signifies at least one end of line.

3   {separator} [In some cases an explicit separator is required to separate
adjacent lexical elements.]  A separator is any of a space character, a
format effector, or the end of a line, as follows:

        3.a   Discussion:  It might be useful to define ``white space'' and
        use it here.

    4  A space character is a separator except within a comment, a
       string_literal, or a character_literal.

    5  Character tabulation (HT) is a separator except within a comment.

    6  The end of a line is always a separator.

7   One or more separators are allowed between any two adjacent lexical
elements, before the first of each compilation, or after the last.  At least
one separator is required between an identifier, a reserved word, or a
numeric_literal and an adjacent identifier, reserved word, or numeric_
literal.

8   {delimiter} A delimiter is either one of the following special characters

9   &    '    (    )    *    +    ,    -    .    /    :    ;    <    =    >    |

10   {compound delimiter} or one of the following compound delimiters each
composed of two adjacent special characters

11  =>    ..    **    :=    /=    >=    <=    <<    >>    <>

12   Each of the special characters listed for single character delimiters is
a single delimiter except if this character is used as a character of a
compound delimiter, or as a character of a comment, string_literal,
character_literal, or numeric_literal.

13   The following names are used when referring to compound delimiters:

14  delimiter     name

       =>                       arrow
       ..                       double dot
       **                       double star, exponentiate
       :=                       assignment (pronounced: ``becomes'')
       /=                       inequality (pronounced: ``not equal'')
       >=                       greater than or equal
       <=                       less than or equal
       <<                       left label bracket
       >>                       right label bracket
       <>                       box


                         Implementation Requirements

15   An implementation shall support lines of at least 200 characters in
length, not counting any characters used to signify the end of a line.  An
implementation shall support lexical elements of at least 200 characters in
length.  The maximum supported line length and lexical element length are
implementation defined.

        15.a   Implementation defined:  Maximum supported line length and
        lexical element length.

        15.b   Discussion:  From URG recommendation.



2.3 Identifiers

1   Identifiers are used as names.


                                   Syntax

2   identifier ::=
       identifier_letter {[underline] letter_or_digit}

3   letter_or_digit ::= identifier_letter | digit

    4   An identifier shall not be a reserved word.


                              Static Semantics

5   All characters of an identifier are significant, including any underline
character.  {case insensitive} Identifiers differing only in the use of
corresponding upper and lower case letters are considered the same.

        5.a   Discussion:  Two of the letters of ISO 8859-1 appear only as
        lower case, "sharp s" and "y with diaeresis."  These two letters have
        no corresponding upper case letter (in particular, they are not
        considered equivalent to one another).


                         Implementation Permissions

6   In a nonstandard mode, an implementation may support other upper/lower
case equivalence rules for identifiers[, to accommodate local conventions].


                                  Examples

7   Examples of identifiers:

8   Count      X    Get_Symbol   Ethelyn   Marion

    Snobol_4   X1   Page_Count    Store_Next_Item


                         Wording Changes From Ada 83

        8.a   We no longer include reserved words as identifiers.  This is
        not a language change.  In Ada 83, identifier included reserved
        words.  However, this complicated several other rules (for example,
        regarding implementation-defined attributes and pragmas, etc.).  We
        now explicitly allow certain reserved words for attribute
        designators, to make up for the loss.

        8.b   Ramification:  Because syntax rules are relevant to overload
        resolution, it means that if it looks like a reserved word, it is not
        an identifier.  As a side effect, implementations cannot use reserved
        words as implementation-defined attributes or pragma names.



2.4 Numeric Literals

1   {literal (numeric)} There are two kinds of numeric_literals, real
literals and integer literals.  {real literal} A real literal is a numeric_
literal that includes a point; {integer literal} an integer literal is a
numeric_literal without a point.


                                   Syntax

2   numeric_literal ::= decimal_literal | based_literal


     NOTES
3    (3) The type of an integer literal is universal_integer.  The type of a
     real literal is universal_real.



2.4.1 Decimal Literals

1   {literal (decimal)} A decimal_literal is a numeric_literal in the
conventional decimal notation (that is, the base is ten).


                                   Syntax

2   decimal_literal ::= numeral [.numeral] [exponent]

3   numeral ::= digit {[underline] digit}

4   exponent ::= E [+] numeral | E - numeral

    5   An exponent for an integer literal shall not have a minus sign.

        5.a   Ramification:  Although this rule is in this subclause, it
        applies also to the next subclause.


                              Static Semantics

6   An underline character in a numeric_literal does not affect its meaning.
The letter E of an exponent can be written either in lower case or in upper
case, with the same meaning.

        6.a   Ramification:  Although these rules are in this subclause, they
        apply also to the next subclause.

7   An exponent indicates the power of ten by which the value of the decimal_
literal without the exponent is to be multiplied to obtain the value of the
decimal_literal with the exponent.


                                  Examples

8   Examples of decimal literals:

9
    12        0      1E6    123_456           --  integer literals

    12.0      0.0    0.456  3.14159_26        --  real literals


                         Wording Changes From Ada 83

        9.a   We have changed the syntactic category name integer to be
        numeral.  We got this idea from ACID.  It avoids the confusion
        between this and integers.  (Other places don't offer similar
        confusions.  For example, a string_literal is different from a
        string.)



2.4.2 Based Literals

1   [{literal (based)} {binary literal} {base 2 literal} {binary (literal)}
{octal literal} {base 8 literal} {octal (literal)} {hexadecimal literal}
{base 16 literal} {hexadecimal (literal)} A based_literal is a numeric_
literal expressed in a form that specifies the base explicitly.]


                                   Syntax

2   based_literal ::=
       base # based_numeral [.based_numeral] # [exponent]
3   base ::= numeral

4   based_numeral ::=
       extended_digit {[underline] extended_digit}

5   extended_digit ::= digit | A | B | C | D | E | F


                               Legality Rules

6   {base} The base (the numeric value of the decimal numeral preceding the
first #) shall be at least two and at most sixteen.  The extended_digits A
through F represent the digits ten through fifteen, respectively.  The value
of each extended_digit of a based_literal shall be less than the base.


                              Static Semantics

7   The conventional meaning of based notation is assumed.  An exponent
indicates the power of the base by which the value of the based_literal
without the exponent is to be multiplied to obtain the value of the based_
literal with the exponent.  The base and the exponent, if any, are in decimal
notation.

8   The extended_digits A through F can be written either in lower case or in
upper case, with the same meaning.


                                  Examples

9   Examples of based literals:

10
    2#1111_1111#   16#FF#       016#0ff#                    --  integer literal\
s of value 255
    16#E#E1        2#1110_0000#                             --  integer literal\
s of value 224
    16#F.FF#E+2    2#1.1111_1111_1110#E11                   --  real literals o\
f value 4095.0


                         Wording Changes From Ada 83

        10.a   The rule about which letters are allowed is now encoded in
        BNF, as suggested by Mike Woodger.  This is clearly more readable.



2.5 Character Literals

1   [A character_literal is formed by enclosing a graphic character between
two apostrophe characters.]


                                   Syntax

2   character_literal ::= 'graphic_character'


     NOTES
3    (4) A character_literal is an enumeration literal of a character type.
     See 3.5.2.


                                  Examples

4   Examples of character literals:

5   'A'     '*'     '''     ' '


                         Wording Changes From Ada 83

        5.a   The definitions of the values of literals are in Sections 3 and
        4, rather than here, since it requires knowledge of types.



2.6 String Literals

1   [A string_literal is formed by a sequence of graphic characters (possibly
none) enclosed between two quotation marks used as string brackets.  They are
used to represent operator_symbols (see 6.1), values of a string type (see
4.2), and array subaggregates (see 4.3.3).  {quoted string: see string_
literal}]


                                   Syntax

2   string_literal ::= "{string_element}"

3   string_element ::= "" | non_quotation_mark_graphic_character

    4   A string_element is either a pair of quotation marks (""), or a
    single graphic_character other than a quotation mark.


                              Static Semantics

5   {sequence of characters (of a string_literal)} The sequence of characters
of a string_literal is formed from the sequence of string_elements between
the bracketing quotation marks, in the given order, with a string_element
that is "" becoming a single quotation mark in the sequence of characters,
and any other string_element being reproduced in the sequence.

6   {null string literal} A null string literal is a string_literal with no
string_elements between the quotation marks.


     NOTES
7    (5) An end of line cannot appear in a string_literal.


                                  Examples

8   Examples of string literals:

9
    "Message of the day:"

    ""                           --  a null string literal
    " "   "A"   """"             --  three string literals of length 1

    "Characters such as $, %, and } are allowed in string literals"


                         Wording Changes From Ada 83

        9.a   The wording has been changed to be strictly lexical.  No
        mention is made of string or character values, since string_literals
        are also used to represent operator_symbols, which don't have a
        defined value.

        9.b   The syntax is described differently.



2.7 Comments

1   A comment starts with two adjacent hyphens and extends up to the end of
the line.


                                   Syntax

2   comment ::= --{non_end_of_line_character}

    3   A comment may appear on any line of a program.


                              Static Semantics

4   The presence or absence of comments has no influence on whether a program
is legal or illegal.  Furthermore, comments do not influence the meaning of a
program; their sole purpose is the enlightenment of the human reader.


                                  Examples

5   Examples of comments:

6   --  the last sentence above echoes the Algol 68 report

    end;  --  processing of Line is complete

    --  a long comment may be split onto
    --  two or more consecutive lines

    ----------------  the first two hyphens start the comment



2.8 Pragmas

1   {Pragma} [glossary entry]A pragma is a compiler directive.  There are
language-defined pragmas that give instructions for optimization, listing
control, etc.  An implementation may support additional (implementation-
defined) pragmas.


                                   Syntax

2   pragma ::=
       pragma identifier [(pragma_argument_association {, pragma_argument_assoc\
iation})];

3   pragma_argument_association ::=
         [pragma_argument_identifier =>] name
       | [pragma_argument_identifier =>] expression

    4   In a pragma, any pragma_argument_associations without a pragma_
    argument_identifier shall precede any associations with a pragma_
    argument_identifier.

    5   Pragmas are only allowed at the following places in a program:

        6  After a semicolon delimiter, but not within a formal_part or
           discriminant_part.

        7  At any place where the syntax rules allow a construct defined
           by a syntactic category whose name ends with "declaration",
           "statement", "clause", or "alternative", or one of the
           syntactic categories variant or exception_handler; but not in
           place of such a construct.  Also at any place where a
           compilation_unit would be allowed.

    8   Additional syntax rules and placement restrictions exist for specific
    pragmas.


        8.a   Discussion:  The above rule is written in text, rather than in
        BNF; the syntactic category pragma is not used in any BNF syntax
        rule.

        8.b   Ramification:  A pragma is allowed where a generic_formal_
        parameter_declaration is allowed.


9   {name (of a pragma)} {pragma name} The name of a pragma is the identifier
following the reserved word pragma.  {pragma argument} {argument of a pragma}
The name or expression of a pragma_argument_association is a pragma argument.

10   {identifier specific to a pragma} {pragma, identifier specific to} An
identifier specific to a pragma is an identifier that is used in a pragma
argument with special meaning for that pragma.

        10.a   To be honest:  Whenever the syntax rules for a given pragma
        allow "identifier" as an argument of the pragma, that identifier is
        an identifier specific to that pragma.


                              Static Semantics

11   If an implementation does not recognize the name of a pragma, then it
has no effect on the semantics of the program.  Inside such a pragma, the
only rules that apply are the Syntax Rules.

        11.a   To be honest:  This rule takes precedence over any other rules
        that imply otherwise.

        11.b   Ramification:  Note well: this rule applies only to pragmas
        whose name is not recognized.  If anything else is wrong with a
        pragma (at compile time), the pragma is illegal.  This is true
        whether the pragma is language defined or implementation defined.

        11.c   For example, an expression in an unrecognized pragma does not
        cause freezing, even though the rules in 13.14, ``Freezing Rules''
        say it does; the above rule overrules those other rules.  On the
        other hand, an expression in a recognized pragma causes freezing,
        even if this makes something illegal.

        11.d   For another example, an expression that would be ambiguous is
        not illegal if it is inside an unrecognized pragma.

        11.e   Note, however, that implementations have to recognize pragma
        Inline(Foo) and freeze things accordingly, even if they choose to
        never do inlining.

        11.f   Obviously, the contradiction needs to be resolved one way or
        the other.  The reasons for resolving it this way are:  The
        implementation is simple -- the compiler can just ignore the pragma
        altogether.  The interpretation of constructs appearing inside
        implementation-defined pragmas is implementation defined.  For
        example: ``pragma Mumble(X);''.  If the current implementation has
        never heard of Mumble, then it doesn't know whether X is a name, an
        expression, or an identifier specific to the pragma Mumble.

        11.g   To be honest:  The syntax of individual pragmas overrides the
        general syntax for pragma.

        11.h   Ramification:  Thus, an identifier specific to a pragma is not
        a name, syntactically; if it were, the visibility rules would be
        invoked, which is not what we want.

        11.i   This also implies that named associations do not allow one to
        give the arguments in an arbitrary order -- the order given in the
        syntax rule for each individual pragma must be obeyed.  However, it
        is generally possible to leave out earlier arguments when later ones
        are given; for example, this is allowed by the syntax rule for pragma
        Import (see B.1, ``Interfacing Pragmas'').  As for subprogram calls,
        positional notation precedes named notation.

        11.j   Note that Ada 83 had no pragmas for which the order of named
        associations mattered, since there was never more than one argument
        that allowed named associations.

        11.k   To be honest:  The interpretation of the arguments of
        implementation-defined pragmas is implementation defined.  However,
        the syntax rules have to be obeyed.


                              Dynamic Semantics

12   {execution [pragma]} {elaboration [pragma]} Any pragma that appears at
the place of an executable construct is executed.  Unless otherwise specified
for a particular pragma, this execution consists of the evaluation of each
evaluable pragma argument in an arbitrary order.

        12.a   Ramification:  For a pragma that appears at the place of an
        elaborable construct, execution is elaboration.

        12.b   An identifier specific to a pragma is neither a name nor an
        expression -- such identifiers are not evaluated (unless an
        implementation defines them to be evaluated in the case of an
        implementation-defined pragma).

        12.c   The ``unless otherwise specified'' part allows us (and
        implementations) to make exceptions, so a pragma can contain an
        expression that is not evaluated.  Note that pragmas in type_
        definitions may contain expressions that depend on discriminants.

        12.d   When we wish to define a pragma with some run-time effect, we
        usually make sure that it appears in an executable context;
        otherwise, special rules are needed to define the run-time effect and
        when it happens.


                         Implementation Requirements

13   The implementation shall give a warning message for an unrecognized
pragma name.

        13.a   Ramification:  An implementation is also allowed to have modes
        in which a warning message is suppressed, or in which the presence of
        an unrecognized pragma is a compile-time error.


                         Implementation Permissions

14   An implementation may provide implementation-defined pragmas; the name
of an implementation-defined pragma shall differ from those of the
language-defined pragmas.

        14.a   Implementation defined:  Implementation-defined pragmas.

        14.b   Ramification:  The semantics of implementation-defined
        pragmas, and any associated rules (such as restrictions on their
        placement or arguments), are, of course, implementation defined.
        Implementation-defined pragmas may have run-time effects.

15   An implementation may ignore an unrecognized pragma even if it violates
some of the Syntax Rules, if detecting the syntax error is too complex.

        15.a   Reason:  Many compilers use extra post-parsing checks to
        enforce the syntax rules, since the Ada syntax rules are not LR(k)
        (for any k).  (The grammar is ambiguous, in fact.)  This paragraph
        allows them to ignore an unrecognized pragma, without having to
        perform such post-parsing checks.


                            Implementation Advice

16   Normally, implementation-defined pragmas should have no semantic effect
for error-free programs; that is, if the implementation-defined pragmas are
removed from a working program, the program should still be legal, and should
still have the same semantics.

        16.a   Ramification:  Note that ``semantics'' is not the same as
        ``effect;'' as explained in 1.1.3, the semantics defines a set of
        possible effects.

        16.b   Note that adding a pragma to a program might cause an error
        (either at compile time or at run time).  On the other hand, if the
        language-specified semantics for a feature are in part implementation
        defined, it makes sense to support pragmas that control the feature,
        and that have real semantics; thus, this paragraph is merely a
        recommendation.

17   Normally, an implementation should not define pragmas that can make an
illegal program legal, except as follows:

   18  A pragma used to complete a declaration, such as a pragma Import;

   19  A pragma used to configure the environment by adding, removing,
       or replacing library_items.

        19.a   Ramification:  For example, it is OK to support Interface,
        System_Name, Storage_Unit, and Memory_Size pragmas for upward
        compatibility reasons, even though all of these pragmas can make an
        illegal program legal.  (The latter three can affect legality in a
        rather subtle way:  They affect the value of named numbers in System,
        and can therefore affect the legality in cases where static
        expressions are required.)

        19.b   On the other hand, adding implementation-defined pragmas to a
        legal program can make it illegal.  For example, a common kind of
        implementation-defined pragma is one that promises some property that
        allows more efficient code to be generated.  If the promise is a lie,
        it is best if the user gets an error message.


                        Incompatibilities With Ada 83

        19.c   {incompatibilities with Ada 83} In Ada 83, ``bad'' pragmas are
        ignored.  In Ada 9X, they are illegal, except in the case where the
        name of the pragma itself is not recognized by the implementation.

                            Extensions to Ada 83

        19.d   {extensions to Ada 83} Implementation-defined pragmas may
        affect the legality of a program.
                         Wording Changes From Ada 83

        19.e   Implementation-defined pragmas may affect the run-time
        semantics of the program.  This was always true in Ada 83 (since it
        was not explicitly forbidden by RM83), but it was not clear, because
        there was no definition of ``executing'' or ``elaborating'' a pragma.

                                   Syntax

    20   The forms of List, Page, and Optimize pragmas are as follows:


21    pragma List(identifier);

22    pragma Page;

23    pragma Optimize(identifier);

    24   [Other pragmas are defined throughout this International Standard,
    and are summarized in Annex L.]

        24.a   Ramification:  The language-defined pragmas are supported by
        every implementation, although ``supporting'' some of them (for
        example, Inline) requires nothing more than checking the arguments,
        since they act only as advice to the implementation.


                              Static Semantics

25   A pragma List takes one of the identifiers On or Off as the single
argument.  This pragma is allowed anywhere a pragma is allowed.  It specifies
that listing of the compilation is to be continued or suspended until a List
pragma with the opposite argument is given within the same compilation.  The
pragma itself is always listed if the compiler is producing a listing.

26   A pragma Page is allowed anywhere a pragma is allowed.  It specifies
that the program text which follows the pragma should start on a new page (if
the compiler is currently producing a listing).

27   A pragma Optimize takes one of the identifiers Time, Space, or Off as
the single argument.  This pragma is allowed anywhere a pragma is allowed,
and it applies until the end of the immediately enclosing declarative region,
or for a pragma at the place of a compilation_unit, to the end of the
compilation.  {94-4761.d} It gives advice to the implementation as to whether
time or space is the primary optimization criterion, or that optional
optimizations should be turned off.  [It is implementation defined how this
advice is followed.]

        27.a   Implementation defined:  Effect of pragma Optimize.

        27.b   Discussion:  For example, a compiler might use Time vs. Space
        to control whether generic instantiations are implemented with a
        macro-expansion model, versus a shared-generic-body model.

        27.c   We don't define what constitutes an ``optimization'' -- in
        fact, it cannot be formally defined in the context of Ada.  One
        compiler might call something an optional optimization, whereas
        another compiler might consider that same thing to be a normal part
        of code generation.  Thus, the programmer cannot rely on this pragma
        having any particular portable effect on the generated code.  Some
        compilers might even ignore the pragma altogether.


                                  Examples

28   Examples of pragmas:

29  pragma List(Off); -- turn off listing generation
    pragma Optimize(Off); -- turn off optional optimizations
    pragma Inline(Set_Mask); -- generate code for Set_Mask inline
    pragma Suppress(Range_Check, On => Index); -- turn off range checking on In\
dex


                            Extensions to Ada 83

        29.a   {extensions to Ada 83} The Optimize pragma now allows the
        identifier Off to request that normal optimization be turned off.

        29.b   An Optimize pragma may appear anywhere pragmas are allowed.

                         Wording Changes From Ada 83

        29.c   We now describe the pragmas Page, List, and Optimize here, to
        act as examples, and to remove the normative material from Annex L,
        ``Language-Defined Pragmas'', so it can be entirely an informative
        annex.
2.9 Reserved Words

                                   Syntax

1
    2   {reserved word} The following are the reserved words (ignoring
    upper/lower case distinctions):


        2.a   Discussion:  Reserved words have special meaning in the syntax.
        In addition, certain reserved words are used as attribute names.

        2.b   The syntactic category identifier no longer allows reserved
        words.  We have added the few reserved words that are legal
        explicitly to the syntax for attribute_reference.  Allowing
        identifier to include reserved words has been a source of confusion
        for some users, and differs from the way they are treated in the C
        and Pascal language definitions.


     abort          else           new            return
     abs            elsif          not            reverse
     abstract       end            null
     accept         entry                         select
     access         exception                     separate
     aliased        exit           of             subtype
     all                           or
     and            for            others         tagged
     array          function       out            task
     at                                           terminate
                    generic        package        then
     begin          goto           pragma         type
     body                          private
                    if             procedure
     case           in             protected      until
     constant       is                            use
                                   raise
     declare                       range          when
     delay          limited        record         while
     delta          loop           rem            with
     digits                        renames
     do             mod            requeue        xor


     NOTES
3    (6) The reserved words appear in lower case boldface in this
     International Standard, except when used in the designator of an
     attribute (see 4.1.4).  Lower case boldface is also used for a reserved
     word in a string_literal used as an operator_symbol.  This is merely a
     convention -- programs may be written in whatever typeface is desired
     and available.  {94-4493.d}


                        Incompatibilities With Ada 83

        3.a   {incompatibilities with Ada 83} The following words are not
        reserved in Ada 83, but are reserved in Ada 9X: abstract, aliased,
        protected, requeue, tagged, until.

                         Wording Changes From Ada 83

        3.b   The clause entitled ``Allowed Replacements of Characters'' has
        been moved to Annex J, ``Obsolescent Features''.



                      Section 3: Declarations and Types


1   This section describes the types in the language and the rules for
declaring constants, variables, and named numbers.



3.1 Declarations

1   {entity [partial]} The language defines several kinds of named entities
that are declared by declarations.  {name [partial]} The entity's name is
defined by the declaration, usually by a defining_identifier, but sometimes
by a defining_character_literal or defining_operator_symbol.

2   There are several forms of declaration.  A basic_declaration is a form of
declaration defined as follows.


                                   Syntax

3   basic_declaration ::=
         type_declaration                 | subtype_declaration
       | object_declaration               | number_declaration
       | subprogram_declaration           | abstract_subprogram_declaration
       | package_declaration              | renaming_declaration
       | exception_declaration            | generic_declaration
       | generic_instantiation

4   defining_identifier ::= identifier


                              Static Semantics

5   {Declaration} [glossary entry]A declaration is a language construct that
associates a name with (a view of) an entity.  {explicit declaration}
{implicit declaration} A declaration may appear explicitly in the program
text (an explicit declaration), or may be supposed to occur at a given place
in the text as a consequence of the semantics of another construct (an
implicit declaration).

        5.a   Discussion:  An implicit declaration generally declares a
        predefined or inherited operation associated with the definition of a
        type.  This term is used primarily when allowing explicit
        declarations to override implicit declarations, as part of a type
        declaration.

6   {declaration} Each of the following is defined to be a declaration:  any
basic_declaration; an enumeration_literal_specification; a discriminant_
specification; a component_declaration; a loop_parameter_specification; a
parameter_specification; a subprogram_body; an entry_declaration; an entry_
index_specification; a choice_parameter_specification; a generic_formal_
parameter_declaration.

        6.a   Discussion:  This list (when basic_declaration is expanded out)
        contains all syntactic categories that end in "_declaration" or
        "_specification", except for program unit _specifications.  Moreover,
        it contains subprogram_body.  A subprogram_body is a declaration,
        whether or not it completes a previous declaration.  This is a bit
        strange, subprogram_body is not part of the syntax of basic_
        declaration or library_unit_declaration.  A renaming-as-body is
        considered a declaration.  An accept_statement is not considered a
        declaration.  Completions are sometimes declarations, and sometimes
        not.

7   {Definition} [glossary entry]{view} All declarations contain a definition
for a view of an entity.  A view consists of an identification of the entity
(the entity of the view), plus view-specific characteristics that affect the
use of the entity through that view (such as mode of access to an object,
formal parameter names and defaults for a subprogram, or visibility to
components of a type).  In most cases, a declaration also contains the
definition for the entity itself (a renaming_declaration is an example of a
declaration that does not define a new entity, but instead defines a view of
an existing entity (see 8.5)).

        7.a   Glossary entry:  {View} (See Definition.)

        7.b   Discussion:  Most declarations define a view (of some entity)
        whose view-specific characteristics are unchanging for the life of
        the view.  However, subtypes are somewhat unusual in that they
        inherit characteristics from whatever view of their type is currently
        visible.  Hence, a subtype is not a view of a type; it is more of an
        indirect reference.  By contrast, a private type provides a single,
        unchanging (partial) view of its full type.

8   {scope [informal definition]} For each declaration, the language rules
define a certain region of text called the scope of the declaration (see
8.2).  Most declarations associate an identifier with a declared entity.
Within its scope, and only there, there are places where it is possible to
use the identifier to refer to the declaration, the view it defines, and the
associated entity; these places are defined by the visibility rules (see
8.3).  {name (of (a view of) an entity)} At such places the identifier is
said to be a name of the entity (the direct_name or selector_name); {denote
[informal definition]} the name is said to denote the declaration, the view,
and the associated entity (see 8.6).  {declare} The declaration is said to
declare the name, the view, and in most cases, the entity itself.

9   As an alternative to an identifier, an enumeration literal can be
declared with a character_literal as its name (see 3.5.1), and a function can
be declared with an operator_symbol as its name (see 6.1).

10   {defining name} The syntax rules use the terms defining_identifier,
defining_character_literal, and defining_operator_symbol for the defining
occurrence of a name; these are collectively called defining names.  {usage
name} The terms direct_name and selector_name are used for usage occurrences
of identifiers, character_literals, and operator_symbols.  These are
collectively called usage names.

        10.a   To be honest:  The terms identifier, character_literal, and
        operator_symbol are used directly in contexts where the normal
        visibility rules do not apply (such as the identifier that appears
        after the end of a task_body).  Analogous conventions apply to the
        use of designator, which is the collective term for identifier and
        operator_symbol.


                              Dynamic Semantics

11   {execution [distributed]} The process by which a construct achieves its
run-time effect is called execution.  {elaboration [distributed]} {evaluation
[distributed]} This process is also called elaboration for declarations and
evaluation for expressions.  One of the terms execution, elaboration, or
evaluation is defined by this International Standard for each construct that
has a run-time effect.

        11.a   Glossary entry:  {Execution} The process by which a construct
        achieves its run-time effect is called execution.  {elaboration}
        {evaluation} Execution of a declaration is also called elaboration.
        Execution of an expression is also called evaluation.

        11.b   To be honest:  The term elaboration is also used for the
        execution of certain constructs that are not declarations, and the
        term evaluation is used for the execution of certain constructs that
        are not expressions.  For example, subtype_indications are
        elaborated, and ranges are evaluated.

        11.c   For bodies, execution and elaboration are both explicitly
        defined.  When we refer specifically to the execution of a body, we
        mean the explicit definition of execution for that kind of body, not
        its elaboration.

        11.d   Discussion:  Technically, "the execution of a declaration" and
        "the elaboration of a declaration" are synonymous.  We use the term
        "elaboration" of a construct when we know the construct is
        elaborable.  When we are talking about more arbitrary constructs, we
        use the term "execution".  For example, we use the term "erroneous
        execution", to refer to any erroneous execution, including erroneous
        elaboration or evaluation.

        11.e   When we explicitly define evaluation or elaboration for a
        construct, we are implicitly defining execution of that construct.

        11.f   We also use the term "execution" for things like statements,
        which are executable, but neither elaborable nor evaluable.  We
        considered using the term "execution" only for non-elaborable,
        non-evaluable constructs, and defining the term "action" to mean what
        we have defined "execution" to mean.  We rejected this idea because
        we thought three terms that mean the same thing was enough -- four
        would be overkill.  Thus, the term "action" is used only informally
        in the standard (except where it is defined as part of a larger term,
        such as "protected action").

        11.g   To be honest:  {elaborable} A construct is elaborable if
        elaboration is defined for it.  {evaluable} A construct is evaluable
        if evaluation is defined for it.  {executable} A construct is
        executable if execution is defined for it.

        11.h   Discussion:  Don't confuse ``elaborable'' with
        ``preelaborable'' (defined in 10.2.1).

        11.i   Evaluation of an evaluable construct produces a result that is
        either a value, a denotation, or a range.  The following are
        evaluable:  expression; name prefix; range; entry_list_iterator; and
        possibly discrete_range.  The last one is curious -- RM83 uses the
        term ``evaluation of a discrete_range,'' but never defines it.  One
        might presume that the evaluation of a discrete_range consists of the
        evaluation of the range or the subtype_indication, depending on what
        it is.  But subtype_indications are not evaluated; they are
        elaborated.

        11.j   Intuitively, an executable construct is one that has a defined
        run-time effect (which may be null).  Since execution includes
        elaboration and evaluation as special cases, all elaborable and all
        evaluable constructs are also executable.  Hence, most constructs in
        Ada are executable.  An important exception is that the constructs
        inside a generic unit are not executable directly, but rather are
        used as a template for (generally) executable constructs in instances
        of the generic.


     NOTES
12   (1) {declare} At compile time, the declaration of an entity declares the
     entity.  {create} At run time, the elaboration of the declaration
     creates the entity.

   12.a   Ramification:  Syntactic categories for declarations are named
        either entity_declaration (if they include a trailing semicolon) or
        entity_specification (if not).

   12.b   {entity} The various kinds of named entities that can be declared
        are as follows: an object (including components and parameters), a
        named number, a type (the name always refers to its first subtype), a
        subtype, a subprogram (including enumeration literals and operators),
        a single entry, an entry family, a package, a protected or task unit
        (which corresponds to either a type or a single object), an
        exception, a generic unit, a label, and the name of a statement.

   12.c   Identifiers are also associated with names of pragmas, arguments to
        pragmas, and with attributes, but these are not user-definable.


                         Wording Changes From Ada 83

        12.d   The syntax rule for defining_identifier is new.  It is used
        for the defining occurrence of an identifier.  Usage occurrences use
        the direct_name or selector_name syntactic categories.  Each
        occurrence of an identifier (or simple_name), character_literal, or
        operator_symbol in the Ada 83 syntax rules is handled as follows in
        Ada 9X:

         12.e  It becomes a defining_identifier, defining_character_
               literal, or defining_operator_symbol (or some syntactic
               category composed of these), to indicate a defining
               occurrence;

         12.f  It becomes a direct_name, in usage occurrences where the
               usage is required (in Section 8) to be directly visible;

         12.g  It becomes a selector_name, in usage occurrences where
               the usage is required (in Section 8) to be visible but
               not necessarily directly visible;

         12.h  It remains an identifier, character_literal, or operator_
               symbol, in cases where the visibility rules do not apply
               (such as the designator that appears after the end of a
               subprogram_body).

        12.i   For declarations that come in ``two parts'' (program unit
        declaration plus body, private or incomplete type plus full type,
        deferred constant plus full constant), we consider both to be
        defining occurrences.  Thus, for example, the syntax for package_body
        uses defining_identifier after the reserved word body, as opposed to
        direct_name.

        12.j   The defining occurrence of a statement name is in its implicit
        declaration, not where it appears in the program text.  Considering
        the statement name itself to be the defining occurrence would
        complicate the visibility rules.

        12.k   The phrase ``visible by selection'' is not used in Ada 9X.  It
        is subsumed by simply ``visible'' and the Name Resolution Rules for
        selector_names.

        12.l   (Note that in Ada 9X, a declaration is visible at all places
        where one could have used a selector_name, not just at places where a
        selector_name was actually used.  Thus, the places where a
        declaration is directly visible are a subset of the places where it
        is visible.  See Section 8 for details.)

        12.m   We use the term ``declaration'' to cover _specifications that
        declare (views of) objects, such as parameter_specifications.  In Ada
        83, these are referred to as a ``form of declaration,'' but it is not
        entirely clear that they are considered simply ``declarations.''

        12.n   RM83 contains an incomplete definition of "elaborated" in this
        clause:  it defines "elaborated" for declarations, declarative_parts,
        declarative_items and compilation_units, but "elaboration" is defined
        elsewhere for various other constructs.  To make matters worse, Ada
        9X has a different set of elaborable constructs.  Instead of
        correcting the list, it is more maintainable to refer to the term
        "elaborable," which is defined in a distributed manner.

        12.o   RM83 uses the term ``has no other effect'' to describe an
        elaboration that doesn't do anything except change the state from
        not-yet-elaborated to elaborated.  This was a confusing wording,
        because the answer to ``other than what?'' was to be found many pages
        away.  In Ada 9X, we change this wording to ``has no effect'' (for
        things that truly do nothing at run time), and ``has no effect other
        than to establish that so-and-so can happen without failing the
        Elaboration_Check'' (for things where it matters).

        12.p   We make it clearer that the term "execution" covers
        elaboration and evaluation as special cases.  This was implied in
        RM83.  For example, "erroneous execution" can include any execution,
        and RM83-9.4(3) has, "The task designated by any other task object
        depends on the master whose execution creates the task object;" the
        elaboration of the master's declarative_part is doing the task
        creation.



3.2 Types and Subtypes

                              Static Semantics

1   {type} {primitive operation [partial]} A type is characterized by a set
of values, and a set of primitive operations which implement the fundamental
aspects of its semantics.  {object [partial]} An object of a given type is a
run-time entity that contains (has) a value of the type.

        1.a   Glossary entry:  {Type} Each object has a type.  A type has an
        associated set of values, and a set of primitive operations which
        implement the fundamental aspects of its semantics.  Types are
        grouped into classes.  The types of a given class share a set of
        primitive operations.  {closed under derivation} Classes are closed
        under derivation; that is, if a type is in a class, then all of its
        derivatives are in that class.

        1.b   Glossary entry:  {Subtype} A subtype is a type together with a
        constraint, which constrains the values of the subtype to satisfy a
        certain condition.  The values of a subtype are a subset of the
        values of its type.

2   {class (of types)} Types are grouped into classes of types, reflecting
the similarity of their values and primitive operations.  {language-defined
class (of types)} There exist several language-defined classes of types (see
NOTES below).  {elementary type} Elementary types are those whose values are
logically indivisible; {composite type} {component} composite types are those
whose values are composed of component values.  {aggregate: see also
composite type}

        2.a   Glossary entry:  {Class} {closed under derivation} A class is a
        set of types that is closed under derivation, which means that if a
        given type is in the class, then all types derived from that type are
        also in the class.  The set of types of a class share common
        properties, such as their primitive operations.

        2.b   Glossary entry:  {Elementary type} An elementary type does not
        have components.

        2.c   Glossary entry:  {Composite type} A composite type has
        components.
        2.d   Glossary entry:  {Scalar type} A scalar type is either a
        discrete type or a real type.

        2.e   Glossary entry:  {Access type} An access type has values that
        designate aliased objects.  Access types correspond to ``pointer
        types'' or ``reference types'' in some other languages.

        2.f   Glossary entry:  {Discrete type} A discrete type is either an
        integer type or an enumeration type.  Discrete types may be used, for
        example, in case_statements and as array indices.

        2.g   Glossary entry:  {Real type} A real type has values that are
        approximations of the real numbers.  Floating point and fixed point
        types are real types.

        2.h   Glossary entry:  {Integer type} Integer types comprise the
        signed integer types and the modular types.  A signed integer type
        has a base range that includes both positive and negative numbers,
        and has operations that may raise an exception when the result is
        outside the base range.  A modular type has a base range whose lower
        bound is zero, and has operations with ``wraparound'' semantics.
        Modular types subsume what are called ``unsigned types'' in some
        other languages.

        2.i   Glossary entry:  {Enumeration type} An enumeration type is
        defined by an enumeration of its values, which may be named by
        identifiers or character literals.

        2.j   Glossary entry:  {Character type} A character type is an
        enumeration type whose values include characters.

        2.k   Glossary entry:  {Record type} A record type is a composite
        type consisting of zero or more named components, possibly of
        different types.

        2.l   Glossary entry:  {Record extension} A record extension is a
        type that extends another type by adding additional components.

        2.m   Glossary entry:  {Array type} An array type is a composite type
        whose components are all of the same type.  Components are selected
        by indexing.

        2.n   Glossary entry:  {Task type} A task type is a composite type
        whose values are tasks, which are active entities that may execute
        concurrently with other tasks.  The top-level task of a partition is
        called the environment task.

        2.o   Glossary entry:  {Protected type} A protected type is a
        composite type whose components are protected from concurrent access
        by multiple tasks.

        2.p   Glossary entry:  {Private type} A private type is a partial
        view of a type whose full view is hidden from its clients.

        2.q   Glossary entry:  {Private extension} A private extension is
        like a record extension, except that the components of the extension
        part are hidden from its clients.

3   {scalar type} The elementary types are the scalar types (discrete and
real) and the access types (whose values provide access to objects or
subprograms).  {discrete type} {enumeration type} Discrete types are either
integer types or are defined by enumeration of their values (enumeration
types).  {real type} Real types are either floating point types or fixed
point types.

4   The composite types are the record types, record extensions, array types,
task types, and protected types.  {private type} {private extension} A
private type or private extension represents a partial view (see 7.3) of a
type, providing support for data abstraction.  A partial view is a composite
type.

        4.a   To be honest:  The set of all record types do not form a class
        (because tagged record types can have private extensions), though the
        set of untagged record types do.  In any case, what record types had
        in common in Ada 83 (component selection) is now a property of the
        composite class, since all composite types (other than array types)
        can have discriminants.  Similarly, the set of all private types do
        not form a class (because tagged private types can have record
        extensions), though the set of untagged private types do.
        Nevertheless, the set of untagged private types is not particularly
        ``interesting'' -- more interesting is the set of all nonlimited
        types, since that is what a generic formal (nonlimited) private type
        matches.

5   {discriminant} Certain composite types (and partial views thereof) have
special components called discriminants whose values affect the presence,
constraints, or initialization of other components.  Discriminants can be
thought of as parameters of the type.

6   {subcomponent} The term subcomponent is used in this International
Standard in place of the term component to indicate either a component, or a
component of another subcomponent.  Where other subcomponents are excluded,
the term component is used instead.  {part (of an object or value)}
Similarly, a part of an object or value is used to mean the whole object or
value, or any set of its subcomponents.

        6.a   Discussion:  The definition of ``part'' here is designed to
        simplify rules elsewhere.  By design, the intuitive meaning of
        ``part'' will convey the correct result to the casual reader, while
        this formalistic definition will answer the concern of the
        compiler-writer.

        6.b   We use the term ``part'' when talking about the parent part,
        ancestor part, or extension part of a type extension.  In contexts
        such as these, the part might represent an empty set of subcomponents
        (e.g. in a null record extension, or a nonnull extension of a null
        record).  We also use ``part'' when specifying rules such as those
        that apply to an object with a ``controlled part'' meaning that it
        applies if the object as a whole is controlled, or any subcomponent
        is.

7   {constraint [partial]} The set of possible values for an object of a
given type can be subjected to a condition that is called a constraint {null
constraint} (the case of a null constraint that specifies no restriction is
also included)[; the rules for which values satisfy a given kind of
constraint are given in 3.5 for range_constraints, 3.6.1 for index_
constraints, and 3.7.1 for discriminant_constraints].

8   {subtype} A subtype of a given type is a combination of the type, a
constraint on values of the type, and certain attributes specific to the
subtype.  The given type is called the type of the subtype.  Similarly, the
associated constraint is called the constraint of the subtype.  The set of
values of a subtype consists of the values of its type that satisfy its
constraint.  {belong (to a subtype)} Such values belong to the subtype.

        8.a   Discussion:  We make a strong distinction between a type and
        its subtypes.  In particular, a type is not a subtype of itself.
        There is no constraint associated with a type (not even a null one),
        and type-related attributes are distinct from subtype-specific
        attributes.

        8.b   Discussion:  We no longer use the term "base type."  All types
        were "base types" anyway in Ada 83, so the term was redundant, and
        occasionally confusing.  In the RM9X we say simply "the type of the
        subtype" instead of "the base type of the subtype."

        8.c   Ramification:  The value subset for a subtype might be empty,
        and need not be a proper subset.

        8.d   To be honest:  Any name of a class of types (such as
        ``discrete'' or ``real''), or other category of types (such as
        ``limited'' or ``incomplete'') is also used to qualify its subtypes,
        as well as its objects, values, declarations, and definitions, such
        as an ``integer type declaration'' or an ``integer value.''  In
        addition, if a term such as ``parent subtype'' or ``index subtype''
        is defined, then the corresponding term for the type of the subtype
        is ``parent type'' or ``index type.''

        8.e   Discussion:  We use these corresponding terms without
        explicitly defining them, when the meaning is obvious.

9   {constrained} {unconstrained} {constrained (subtype)} {unconstrained
(subtype)} A subtype is called an unconstrained subtype if its type has
unknown discriminants, or if its type allows range, index, or discriminant
constraints, but the subtype does not impose such a constraint; otherwise,
the subtype is called a constrained subtype (since it has no unconstrained
characteristics).

        9.a   Discussion:  In an earlier version of Ada 9X, "constrained"
        meant "has a non-null constraint."  However, we changed to this
        definition since we kept having to special case composite
        non-array/non-discriminated types.  It also corresponds better to the
        (now obsolescent) attribute 'Constrained.

        9.b   For scalar types, ``constrained'' means ``has a non-null
        constraint''.  For composite types, in implementation terms,
        ``constrained'' means that the size of all objects of the subtype is
        the same, assuming a typical implementation model.

        9.c   Class-wide subtypes are always unconstrained.


     NOTES
10   (2) Any set of types that is closed under derivation (see 3.4) can be
     called a ``class'' of types.  However, only certain classes are used in
     the description of the rules of the language -- generally those that
     have their own particular set of primitive operations (see 3.2.3), or
     that correspond to a set of types that are matched by a given kind of
     generic formal type (see 12.5).  {language-defined class [partial]} The
     following are examples of ``interesting'' language-defined classes:
     elementary, scalar, discrete, enumeration, character, boolean, integer,
     signed integer, modular, real, floating point, fixed point, ordinary
     fixed point, decimal fixed point, numeric, access, access-to-object,
     access-to-subprogram, composite, array, string, (untagged) record,
     tagged, task, protected, nonlimited.  Special syntax is provided to
     define types in each of these classes.

        10.a   Discussion:  {value} A value is a run-time entity with a given
        type which can be assigned to an object of an appropriate subtype of
        the type.  {operation} An operation is a program entity that operates
        on zero or more operands to produce an effect, or yield a result, or
        both.

        10.b   Ramification:  Note that a type's class depends on the place
        of the reference -- a private type is composite outside and possibly
        elementary inside.  It's really the view that is elementary or
        composite.  Note that although private types are composite, there are
        some properties that depend on the corresponding full view -- for
        example, parameter passing modes, and the constraint checks that
        apply in various places.

        10.c   Not every property of types represents a class.  For example,
        the set of all abstract types does not form a class, because this set
        is not closed under derivation.

        10.d   The set of limited types forms a class in the sense that it is
        closed under derivation, but the more interesting class, from the
        point of generic formal type matching, is the set of all types,
        limited and nonlimited, since that is what matches a generic formal
        ``limited'' private type.  Note also that a limited type can ``become
        nonlimited'' under certain circumstances, which makes ``limited''
        somewhat problematic as a class of types.

     11   These language-defined classes are organized like this:

12
         all types
            elementary
               scalar
                  discrete
                     enumeration
                        character
                        boolean
                        other enumeration
                     integer
                        signed integer
                        modular integer
                  real
                     floating point
                     fixed point
                        ordinary fixed point
                        decimal fixed point
               access
                  access-to-object
                  access-to-subprogram
            composite
               array
                  string
                  other array
               untagged record
               tagged
               task
               protected

     13   The classes ``numeric'' and ``nonlimited'' represent other
     classification dimensions and do not fit into the above strictly
     hierarchical picture.


                         Wording Changes From Ada 83

        13.a   This clause and its subclauses now precede the clause and
        subclauses on objects and named numbers, to cut down on the number of
        forward references.

        13.b   We have dropped the term "base type" in favor of simply "type"
        (all types in Ada 83 were "base types" so it wasn't clear when it was
        appropriate/necessary to say "base type").  Given a subtype S of a
        type T, we call T the "type of the subtype S."



3.2.1 Type Declarations

1   A type_declaration declares a type and its first subtype.


                                   Syntax

2   type_declaration ::=  full_type_declaration
       | incomplete_type_declaration
       | private_type_declaration
       | private_extension_declaration

3   full_type_declaration ::=
         type defining_identifier [known_discriminant_part] is type_definition;
       | task_type_declaration
       | protected_type_declaration

4   type_definition ::=
         enumeration_type_definition | integer_type_definition
       | real_type_definition        | array_type_definition
       | record_type_definition      | access_type_definition
       | derived_type_definition


                               Legality Rules

5   A given type shall not have a subcomponent whose type is the given type
itself.


                              Static Semantics

6   {first subtype} The defining_identifier of a type_declaration denotes the
first subtype of the type.  The known_discriminant_part, if any, defines the
discriminants of the type (see 3.7, ``Discriminants'').  The remainder of the
type_declaration defines the remaining characteristics of (the view of) the
type.

7   {named type} A type defined by a type_declaration is a named type; such a
type has one or more nameable subtypes.  {anonymous type} Certain other forms
of declaration also include type definitions as part of the declaration for
an object (including a parameter or a discriminant).  The type defined by
such a declaration is anonymous -- it has no nameable subtypes.  {italics
(pseudo-names of anonymous types)} For explanatory purposes, this
International Standard sometimes refers to an anonymous type by a
pseudo-name, written in italics, and uses such pseudo-names at places where
the syntax normally requires an identifier.  For a named type whose first
subtype is T, this International Standard sometimes refers to the type of T
as simply ``the type T.''

        7.a   Ramification:  The only user-defined types that can be
        anonymous in the above sense are array, access, task, and protected
        types.  An anonymous array, task, or protected type can be defined as
        part of an object_declaration.  An anonymous access type can be
        defined as part of a parameter or discriminant specification.

8   {full type} A named type that is declared by a full_type_declaration, or
an anonymous type that is defined as part of declaring an object of the type,
is called a full type.  {full type definition} The type_definition, task_
definition, protected_definition, or access_definition that defines a full
type is called a full type definition.[Types declared by other forms of type_
declaration are not separate types; they are partial or incomplete views of
some full type.]

        8.a   To be honest:  Class-wide, universal, and root numeric types
        are full types.

9   {predefined operator [partial]} The definition of a type implicitly
declares certain predefined operators that operate on the type, according to
what classes the type belongs, as specified in 4.5, ``Operators and
Expression Evaluation''.

        9.a   Discussion:  We no longer talk about the implicit declaration
        of basic operations.  These are treated like an if_statement -- they
        don't need to be declared, but are still applicable to only certain
        classes of types.

10   {predefined type} The predefined types [(for example the types Boolean,
Wide_Character, Integer, root_integer, and universal_integer)] are the types
that are defined in [a predefined library package called] Standard[; this
package also includes the [(implicit)] declarations of their predefined
operators].  [The package Standard is described in A.1.]

        10.a   Ramification:  We use the term ``predefined'' to refer to
        entities declared in the visible part of Standard, to implicitly
        declared operators of a type whose semantics are defined by the
        language, to Standard itself, and to the ``predefined environment''.
        We do not use this term to refer to library packages other than
        Standard.  For example Text_IO is a language-defined package, not a
        predefined package, and Text_IO.Put_Line is not a predefined
        operation.


                              Dynamic Semantics

11   {elaboration [full_type_declaration]} The elaboration of a full_type_
declaration consists of the elaboration of the full type definition.
{elaboration [full type definition]} Each elaboration of a full type
definition creates a distinct type and its first subtype.

        11.a   Reason:  The creation is associated with the type definition,
        rather than the type declaration, because there are types that are
        created by full type definitions that are not immediately contained
        within a type declaration (e.g.  an array object declaration, a
        singleton task declaration, etc.).

        11.b   Ramification:  Any implicit declarations that occur
        immediately following the full type definition are elaborated where
        they (implicitly) occur.


                                  Examples

12   Examples of type definitions:

13  (White, Red, Yellow, Green, Blue, Brown, Black)
    range 1 .. 72
    array(1 .. 10) of Integer

14   Examples of type declarations:

15  type Color  is (White, Red, Yellow, Green, Blue, Brown, Black);
    type Column is range 1 .. 72;
    type Table  is array(1 .. 10) of Integer;


     NOTES
16   (3) Each of the above examples declares a named type.  The identifier
     given denotes the first subtype of the type.  Other named subtypes of
     the type can be declared with subtype_declarations (see 3.2.2).
     Although names do not directly denote types, a phrase like ``the type
     Column'' is sometimes used in this International Standard to refer to
     the type of Column, where Column denotes the first subtype of the type.
     For an example of the definition of an anonymous type, see the
     declaration of the array Color_Table in 3.3.1; its type is anonymous --
     it has no nameable subtypes.
                         Wording Changes From Ada 83

        16.a   The syntactic category full_type_declaration now includes task
        and protected type declarations.

        16.b   We have generalized the concept of first-named subtype (now
        called simply ``first subtype'') to cover all kinds of types, for
        uniformity of description elsewhere.  RM83 defined first-named
        subtype in Section 13.  We define first subtype here, because it is
        now a more fundamental concept.  We renamed the term, because in Ada
        9X some first subtypes have no name.

        16.c   We no longer elaborate discriminant_parts, because there is
        nothing to do, and it was complex to say that you only wanted to
        elaborate it once for a private or incomplete type.  This is also
        consistent with the fact that subprogram specifications are not
        elaborated (neither in Ada 83 nor in Ada 9X).  Note, however, that an
        access_definition appearing in a discriminant_part is elaborated when
        an object with such a discriminant is created.



3.2.2 Subtype Declarations

1   A subtype_declaration declares a subtype of some previously declared
type, as defined by a subtype_indication.


                                   Syntax

2   subtype_declaration ::=
       subtype defining_identifier is subtype_indication;

3   subtype_indication ::=  subtype_mark [constraint]

4   subtype_mark ::= subtype_name

        4.a   Ramification:  Note that name includes attribute_reference;
        thus, S'Base can be used as a subtype_mark.

        4.b   Reason:  We considered changing subtype_mark to subtype_name.
        However, existing users are used to the word "mark," so we're keeping
        it.

5   constraint ::= scalar_constraint | composite_constraint

6   scalar_constraint ::=
         range_constraint | digits_constraint | delta_constraint

7   composite_constraint ::=
         index_constraint | discriminant_constraint


                            Name Resolution Rules

8   A subtype_mark shall resolve to denote a subtype.  {determines (a type by
a subtype_mark)} The type determined by a subtype_mark is the type of the
subtype denoted by the subtype_mark.

        8.a   Ramification:  Types are never directly named; all subtype_
        marks denote subtypes -- possibly an unconstrained (base) subtype,
        but never the type.  When we use the term anonymous type we really
        mean a type with no namable subtypes.


                              Dynamic Semantics

9   {elaboration [subtype_declaration]} The elaboration of a subtype_
declaration consists of the elaboration of the subtype_indication.
{elaboration [subtype_indication]} The elaboration of a subtype_indication
creates a new subtype.  If the subtype_indication does not include a
constraint, the new subtype has the same (possibly null) constraint as that
denoted by the subtype_mark.  The elaboration of a subtype_indication that
includes a constraint proceeds as follows:

   10  The constraint is first elaborated.

   11  {Range_Check [partial]} {check, language-defined (Range_Check)} A
       check is then made that the constraint is compatible with the
       subtype denoted by the subtype_mark.

 11.a   Ramification:  The checks associated with constraint
        compatibility are all Range_Checks.  Discriminant_Checks and
        Index_Checks are associated only with checks that a value
        satisfies a constraint.

12   The condition imposed by a constraint is the condition obtained after
elaboration of the constraint.  {compatibility (constraint with a subtype)
[distributed]} The rules defining compatibility are given for each form of
constraint in the appropriate subclause.  These rules are such that if a
constraint is compatible with a subtype, then the condition imposed by the
constraint cannot contradict any condition already imposed by the subtype on
its values.  {Constraint_Error (raised by failure of run-time check)} The
exception Constraint_Error is raised if any check of compatibility fails.

        12.a   To be honest:  The condition imposed by a constraint is named
        after it -- a range_constraint imposes a range constraint, etc.

        12.b   Ramification:  A range_constraint causes freezing of its type.
        Other constraints do not.


     NOTES
13   (4) A scalar_constraint may be applied to a subtype of an appropriate
     scalar type (see 3.5, 3.5.9, and J.3), even if the subtype is already
     constrained.  On the other hand, a composite_constraint may be applied
     to a composite subtype (or an access-to-composite subtype) only if the
     composite subtype is unconstrained (see 3.6.1 and 3.7.1).


                                  Examples

14   Examples of subtype declarations:

15  subtype Rainbow   is Color range Red .. Blue;        --  see 3.2.1
    subtype Red_Blue  is Rainbow;
    subtype Int       is Integer;
    subtype Small_Int is Integer range -10 .. 10;
    subtype Up_To_K   is Column range 1 .. K;            --  see 3.2.1
    subtype Square    is Matrix(1 .. 10, 1 .. 10);       --  see 3.6
    subtype Male      is Person(Sex => M);               --  see 3.10.1


                        Incompatibilities With Ada 83

        15.a   {incompatibilities with Ada 83} In Ada 9X, all range_
        constraints cause freezing of their type.  Hence, a type-related
        representation item for a scalar type has to precede any range_
        constraints whose type is the scalar type.

                         Wording Changes From Ada 83

        15.b   Subtype_marks allow only subtype names now, since types are
        never directly named.  There is no need for RM83-3.3.2(3), which says
        a subtype_mark can denote both the type and the subtype; in Ada 9X,
        you denote an unconstrained (base) subtype if you want, but never the
        type.

        15.c   The syntactic category type_mark is now called subtype_mark,
        since it always denotes a subtype.



3.2.3 Classification of Operations

                              Static Semantics

1   {operates on a type} An operation operates on a type T if it yields a
value of type T, if it has an operand whose expected type (see 8.6) is T, or
if it has an access parameter (see 6.1) designating T.  {predefined operation
(of a type)} A predefined operator, or other language-defined operation such
as assignment or a membership test, that operates on a type, is called a
predefined operation of the type.  {primitive operations (of a type)} The
primitive operations of a type are the predefined operations of the type,
plus any user-defined primitive subprograms.

        1.a   Glossary entry:  {Primitive operations} The primitive
        operations of a type are the operations (such as subprograms)
        declared together with the type declaration.  They are inherited by
        other types in the same class of types.  For a tagged type, the
        primitive subprograms are dispatching subprograms, providing run-time
        polymorphism.  A dispatching subprogram may be called with statically
        tagged operands, in which case the subprogram body invoked is
        determined at compile time.  Alternatively, a dispatching subprogram
        may be called using a dispatching call, in which case the subprogram
        body invoked is determined at run time.

        1.b   To be honest:  Protected subprograms are not considered to be
        ``primitive subprograms,'' even though they are subprograms, and they
        are inherited by derived types.

        1.c   Discussion:  We use the term ``primitive subprogram'' in most
        of the rest of the manual.  The term ``primitive operation'' is used
        mostly in conceptual discussions.

2   {primitive subprograms (of a type)} The primitive subprograms of a
specific type are defined as follows:

    3  The predefined operators of the type (see 4.5);

    4  For a derived type, the inherited (see 3.4) user-defined
       subprograms;

    5  For an enumeration type, the enumeration literals (which are
       considered parameterless functions -- see 3.5.1);

    6  For a specific type declared immediately within a package_
       specification, any subprograms (in addition to the enumeration
       literals) that are explicitly declared immediately within the
       same package_specification and that operate on the type;

    7  {override (a primitive subprogram)} Any subprograms not covered
       above [that are explicitly declared immediately within the same
       declarative region as the type] and that override (see 8.3) other
       implicitly declared primitive subprograms of the type.
       {94-4450.a} {94-4451.a} {94-4453.a}

        7.a   Discussion:  In Ada 83, only subprograms declared in the
        visible part were ``primitive'' (i.e.  derivable).  In Ada 9X, mostly
        because of child library units, we include all operations declared in
        the private part as well, and all operations that override implicit
        declarations.

        7.b   Ramification:  It is possible for a subprogram to be primitive
        for more than one type, though it is illegal for a subprogram to be
        primitive for more than one tagged type.  See 3.9.

        7.c   Discussion:  The order of the implicit declarations when there
        are both predefined operators and inherited subprograms is described
        in 3.4, ``Derived Types and Classes''.

8   {primitive operator (of a type)} A primitive subprogram whose designator
is an operator_symbol is called a primitive operator.


                        Incompatibilities With Ada 83

        8.a   {incompatibilities with Ada 83} The attribute S'Base is no
        longer defined for non-scalar subtypes.  Since this was only
        permitted as the prefix of another attribute, and there are no
        interesting non-scalar attributes defined for an unconstrained
        composite or access subtype, this should not affect any existing
        programs.

                            Extensions to Ada 83

        8.b   {extensions to Ada 83} The primitive subprograms (derivable
        subprograms) include subprograms declared in the private part of a
        package specification as well, and those that override implicitly
        declared subprograms, even if declared in a body.

                         Wording Changes From Ada 83

        8.c   We have dropped the confusing term operation of a type in favor
        of the more useful primitive operation of a type and the phrase
        operates on a type.

        8.d   The description of S'Base has been moved to 3.5, ``Scalar
        Types'' because it is now defined only for scalar types.



3.3 Objects and Named Numbers

1   [Objects are created at run time and contain a value of a given type.
{creation (of an object)} An object can be created and initialized as part of
elaborating a declaration, evaluating an allocator, aggregate, or function_
call, or passing a parameter by copy.  Prior to reclaiming the storage for an
object, it is finalized if necessary (see 7.6.1).]


                              Static Semantics

2   {object} All of the following are objects:

        2.a   Glossary entry:  {Object} An object is either a constant or a
        variable.  An object contains a value.  An object is created by an
        object_declaration or by an allocator.  A formal parameter is (a view
        of) an object.  A subcomponent of an object is an object.

    3  the entity declared by an object_declaration;

    4  a formal parameter of a subprogram, entry, or generic subprogram;

    5  a generic formal object;

    6  a loop parameter;

    7  a choice parameter of an exception_handler;

    8  an entry index of an entry_body;

    9  the result of dereferencing an access-to-object value (see 4.1);

   10  the result of evaluating a function_call (or the equivalent
       operator invocation -- see 6.6);

   11  the result of evaluating an aggregate;

   12  a component, slice, or view conversion of another object.

13   {constant} {variable} {constant object} {variable object} {constant
view} {variable view} An object is either a constant object or a variable
object.  The value of a constant object cannot be changed between its
initialization and its finalization, whereas the value of a variable object
can be changed.  Similarly, a view of an object is either a constant or a
variable.  All views of a constant object are constant.  A constant view of a
variable object cannot be used to modify the value of the variable.  The
terms constant and variable by themselves refer to constant and variable
views of objects.

14   {read (the value of an object)} The value of an object is read when the
value of any part of the object is evaluated, or when the value of an
enclosing object is evaluated.  {update (the value of an object)} The value
of a variable is updated when an assignment is performed to any part of the
variable, or when an assignment is performed to an enclosing object.

        14.a   Ramification:  Reading and updating are intended to include
        read/write references of any kind, even if they are not associated
        with the evaluation of a particular construct.  Consider, for
        example, the expression ``X.all(F)'', where X is an access-to-array
        object, and F is a function.  The implementation is allowed to first
        evaluate ``X.all'' and then F. Finally, a read is performed to get
        the value of the F'th component of the array.  Note that the array is
        not necessarily read as part of the evaluation of ``X.all''.  This is
        important, because if F were to free X using Unchecked_Deallocation,
        we want the execution of the final read to be erroneous.

15   Whether a view of an object is constant or variable is determined by the
definition of the view.  The following (and no others) represent constants:

   16  an object declared by an object_declaration with the reserved
       word constant;

   17  a formal parameter or generic formal object of mode in;

   18  a discriminant;

   19  a loop parameter, choice parameter, or entry index;

   20  the dereference of an access-to-constant value;

   21  the result of evaluating a function_call or an aggregate;

   22  a selected_component, indexed_component, slice, or view
       conversion of a constant.

 22.a   To be honest:  A noninvertible view conversion to a general
        access type is also defined to be a constant -- see 4.6.

23   {nominal subtype} At the place where a view of an object is defined, a
nominal subtype is associated with the view.  {actual subtype} {subtype (of
an object): see actual subtype of an object} The object's actual subtype
(that is, its subtype) can be more restrictive than the nominal subtype of
the view; it always is if the nominal subtype is an indefinite subtype.
{indefinite subtype} {definite subtype} A subtype is an indefinite subtype if
it is an unconstrained array subtype, or if it has unknown discriminants or
unconstrained discriminants without defaults (see 3.7); otherwise the subtype
is a definite subtype [(all elementary subtypes are definite subtypes)].[A
class-wide subtype is defined to have unknown discriminants, and is therefore
an indefinite subtype.  An indefinite subtype does not by itself provide
enough information to create an object; an additional constraint or explicit
initialization expression is necessary (see 3.3.1).  A component cannot have
an indefinite nominal subtype.  {94-4799.a}]

24   {named number} A named number provides a name for a numeric value known
at compile time.  It is declared by a number_declaration.


     NOTES
25   (5) A constant cannot be the target of an assignment operation, nor be
     passed as an in out or out parameter, between its initialization and
     finalization, if any.

26   (6) The nominal and actual subtypes of an elementary object are always
     the same.  For a discriminated or array object, if the nominal subtype
     is constrained then so is the actual subtype.


                            Extensions to Ada 83

        26.a   {extensions to Ada 83} There are additional kinds of objects
        (choice parameters and entry indices of entry bodies).

        26.b   The result of a function and of evaluating an aggregate are
        considered (constant) objects.  This is necessary to explain the
        action of finalization on such things.  Because a function_call is
        also syntactically a name (see 4.1), the result of a function_call
        can be renamed, thereby allowing repeated use of the result without
        calling the function again.

                         Wording Changes From Ada 83

        26.c   This clause and its subclauses now follow the clause and
        subclauses on types and subtypes, to cut down on the number of
        forward references.

        26.d   The term nominal subtype is new.  It is used to distinguish
        what is known at compile time about an object's constraint, versus
        what its "true" run-time constraint is.

        26.e   The terms definite and indefinite (which apply to subtypes)
        are new.  They are used to aid in the description of generic formal
        type matching, and to specify when an explicit initial value is
        required in an object_declaration.

        26.f   We have moved the syntax for object_declaration and number_
        declaration down into their respective subclauses, to keep the syntax
        close to the description of the associated semantics.

        26.g   We talk about variables and constants here, since the
        discussion is not specific to object_declarations, and it seems
        better to have the list of the kinds of constants juxtaposed with the
        kinds of objects.

        26.h   We no longer talk about indirect updating due to parameter
        passing.  Parameter passing is handled in 6.2 and 6.4.1 in a way that
        there is no need to mention it here in the definition of read and
        update.  Reading and updating now includes the case of evaluating or
        assigning to an enclosing object.
3.3.1 Object Declarations

1   {stand-alone object} {explicit initial value} {initialization expression}
An object_declaration declares a stand-alone object with a given nominal
subtype and, optionally, an explicit initial value given by an initialization
expression.  {anonymous array type} {anonymous task type} {anonymous
protected type} For an array, task, or protected object, the object_
declaration may include the definition of the (anonymous) type of the object.


                                   Syntax

2   object_declaration ::=
        defining_identifier_list : [aliased] [constant] subtype_indication [:= \
expression];
      | defining_identifier_list : [aliased] [constant] array_type_definition [\
:= expression];
      | single_task_declaration
      | single_protected_declaration

3   defining_identifier_list ::=
      defining_identifier {, defining_identifier}


                            Name Resolution Rules

4   {expected type [object_declaration initialization expression]} For an
object_declaration with an expression following the compound delimiter :=,
the type expected for the expression is that of the object.  {initialization
expression} This expression is called the initialization expression.
{constructor: see initialization expression}


                               Legality Rules

5   An object_declaration without the reserved word constant declares a
variable object.  If it has a subtype_indication or an array_type_definition
that defines an indefinite subtype, then there shall be an initialization
expression.  An initialization expression shall not be given if the object is
of a limited type.


                              Static Semantics

6   An object_declaration with the reserved word constant declares a constant
object.  {full constant declaration} If it has an initialization expression,
then it is called a full constant declaration.  {deferred constant
declaration} Otherwise it is called a deferred constant declaration.  The
rules for deferred constant declarations are given in clause 7.4.  The rules
for full constant declarations are given in this subclause.

7   Any declaration that includes a defining_identifier_list with more than
one defining_identifier is equivalent to a series of declarations each
containing one defining_identifier from the list, with the rest of the text
of the declaration copied for each declaration in the series, in the same
order as the list.  The remainder of this International Standard relies on
this equivalence; explanations are given for declarations with a single
defining_identifier.

8   {nominal subtype} The subtype_indication or full type definition of an
object_declaration defines the nominal subtype of the object.  The object_
declaration declares an object of the type of the nominal subtype.

        8.a   Discussion:  The phrase ``full type definition'' here includes
        the case of an anonymous array, task, or protected type.


                              Dynamic Semantics

9   {constraint (of an object)} If a composite object declared by an object_
declaration has an unconstrained nominal subtype, then if this subtype is
indefinite or the object is constant or aliased (see 3.10) the actual subtype
of this object is constrained.  The constraint is determined by the bounds or
discriminants (if any) of its initial value; {constrained by its initial
value} the object is said to be constrained by its initial value.  {actual
subtype (of an object)} {subtype (of an object): see actual subtype of an
object} [In the case of an aliased object, this initial value may be either
explicit or implicit; in the other cases, an explicit initial value is
required.]  {94-4858.a} When not constrained by its initial value, the actual
and nominal subtypes of the object are the same.  {constrained (object)}
{unconstrained (object)} If its actual subtype is constrained, the object is
called a constrained object.

10   {implicit initial values (for a subtype)} For an object_declaration
without an initialization expression, any initial values for the object or
its subcomponents are determined by the implicit initial values defined for
its nominal subtype, as follows:

   11  The implicit initial value for an access subtype is the null
       value of the access type.

   12  The implicit initial (and only) value for each discriminant of a
       constrained discriminated subtype is defined by the subtype.

   13  For a (definite) composite subtype, the implicit initial value of
       each component with a default_expression is obtained by
       evaluation of this expression and conversion to the component's
       nominal subtype (which might raise Constraint_Error -- see 4.6,
       ``Type Conversions''), unless the component is a discriminant of
       a constrained subtype (the previous case), or is in an excluded
       variant (see 3.8.1).  {implicit subtype conversion [component
       defaults]} For each component that does not have a default_
       expression, any implicit initial values are those determined by
       the component's nominal subtype.

   14  For a protected or task subtype, there is an implicit component
       (an entry queue) corresponding to each entry, with its implicit
       initial value being an empty queue.

 14.a   Implementation Note:  The implementation may add implicit
        components for its own use, which might have implicit initial
        values.  For a task subtype, such components might represent the
        state of the associated thread of control.  For a type with
        dynamic-sized components, such implicit components might be used
        to hold the offset to some explicit component.

15   {elaboration [object_declaration]} The elaboration of an object_
declaration proceeds in the following sequence of steps:

   16  The subtype_indication, array_type_definition, single_task_
       declaration, or single_protected_declaration is first elaborated.
       This creates the nominal subtype (and the anonymous type in the
       latter three cases).

   17  If the object_declaration includes an initialization expression,
       the (explicit) initial value is obtained by evaluating the
       expression and converting it to the nominal subtype (which might
       raise Constraint_Error -- see 4.6).  {implicit subtype conversion
       [initialization expression]}

   18  The object is created, and, if there is not an initialization
       expression, any per-object expressions (see 3.8) are evaluated
       and any implicit initial values for the object or for its
       subcomponents are obtained as determined by the nominal subtype.

 18.a   Discussion:  For a per-object constraint that contains some
        per-object expressions and some non-per-object expressions, the
        values used for the constraint consist of the values of the
        non-per-object expressions evaluated at the point of the type_
        declaration, and the values of the per-object expressions
        evaluated at the point of the creation of the object.

 18.b   The elaboration of per-object constraints was presumably
        performed as part of the dependent compatibility check in Ada
        83.  If the object is of a limited type with an access
        discriminant, the access_definition is elaborated at this time
        (see 3.7).

 18.c   Reason:  The reason we say that evaluating an explicit
        initialization expression happens before creating the object is
        that in some cases it is impossible to know the size of the
        object being created until its initial value is known, as in
        ``X: String := Func_Call(...);''.  The implementation can create
        the object early in the common case where the size can be known
        early, since this optimization is semantically neutral.

   19  {initialization (of an object)} {assignment operation (during
       elaboration of an object_declaration)} Any initial values
       (whether explicit or implicit) are assigned to the object or to
       the corresponding subcomponents.  As described in 5.2 and 7.6,
       Initialize and Adjust procedures can be called.  {constructor:
       see initialization}

 19.a   Ramification:  Since the initial values have already been
        converted to the appropriate nominal subtype, the only
        Constraint_Errors that might occur as part of these assignments
        are for values outside their base range that are used to
        initialize unconstrained numeric subcomponents.  See 3.5.

20   For the third step above, the object creation and any elaborations and
evaluations are performed in an arbitrary order, except that if the default_
expression for a discriminant is evaluated to obtain its initial value, then
this evaluation is performed before that of the default_expression for any
component that depends on the discriminant, and also before that of any
default_expression that includes the name of the discriminant.  The
evaluations of the third step and the assignments of the fourth step are
performed in an arbitrary order, except that each evaluation is performed
before the resulting value is assigned.

        20.a   Reason:  For example:

20.b        type R(D : Integer := F) is
                record
                    S : String(1..D) := (others => G);
                end record;

20.c        X : R;

        20.d   For the elaboration of the declaration of X, it is important
        that F be evaluated before the aggregate.

21   [There is no implicit initial value defined for a scalar subtype.]
{uninitialized variables [partial]} In the absence of an explicit
initialization, a newly created scalar object might have a value that does
not belong to its subtype (see 13.9.1 and H.1).

        21.a   To be honest:  It could even be represented by a bit pattern
        that doesn't actually represent any value of the type at all, such as
        an invalid internal code for an enumeration type, or a NaN for a
        floating point type.  It is a generally a bounded error to reference
        scalar objects with such ``invalid representations'', as explained in
        13.9.1, ``Data Validity''.
        21.b   Ramification:  There is no requirement that two objects of the
        same scalar subtype have the same implicit initial ``value'' (or
        representation).  It might even be the case that two elaborations of
        the same object_declaration produce two different initial values.
        However, any particular uninitialized object is default-initialized
        to a single value (or invalid representation).  Thus, multiple reads
        of such an uninitialized object will produce the same value each time
        (if the implementation chooses not to detect the error).


     NOTES
22   (7) Implicit initial values are not defined for an indefinite subtype,
     because if an object's nominal subtype is indefinite, an explicit
     initial value is required.  {94-4799.a}

23   (8) {stand-alone constant} {stand-alone variable} As indicated above, a
     stand-alone object is an object declared by an object_declaration.
     Similar definitions apply to ``stand-alone constant'' and ``stand-alone
     variable.''  A subcomponent of an object is not a stand-alone object,
     nor is an object that is created by an allocator.  An object declared by
     a loop_parameter_specification, parameter_specification, entry_index_
     specification, choice_parameter_specification, or a formal_object_
     declaration is not called a stand-alone object.

24   (9) The type of a stand-alone object cannot be abstract (see 3.9.3).


                                  Examples

25   Example of a multiple object declaration:

26  --  the multiple object declaration

27  John, Paul : Person_Name := new Person(Sex => M);  --  see 3.10.1

28  --  is equivalent to the two single object declarations in the order given

29  John : Person_Name := new Person(Sex => M);
    Paul : Person_Name := new Person(Sex => M);

30   Examples of variable declarations:

31  Count, Sum  : Integer;
    Size        : Integer range 0 .. 10_000 := 0;
    Sorted      : Boolean := False;
    Color_Table : array(1 .. Max) of Color;
    Option      : Bit_Vector(1 .. 10) := (others => True);
    Hello       : constant String := "Hi, world.";

32   Examples of constant declarations:

33  Limit     : constant Integer := 10_000;
    Low_Limit : constant Integer := Limit/10;
    Tolerance : constant Real := Dispersion(1.15);


                            Extensions to Ada 83

        33.a   {extensions to Ada 83} The syntax rule for object_declaration
        is modified to allow the aliased reserved word.

        33.b   A variable declared by an object_declaration can be
        constrained by its initial value; that is, a variable of a nominally
        unconstrained array subtype, or discriminated type without defaults,
        can be declared so long as it has an explicit initial value.  In Ada
        83, this was permitted for constants, and for variables created by
        allocators, but not for variables declared by object_declarations.
        This is particularly important for tagged class-wide types, since
        there is no way to constrain them explicitly, and so an initial value
        is the only way to provide a constraint.  It is also important for
        generic formal private types with unknown discriminants.

        33.c   We now allow an unconstrained_array_definition in an object_
        declaration.  This allows an object of an anonymous array type to
        have its bounds determined by its initial value.  This is for
        uniformity: If one can write ``X: constant array(Integer range 1..10)
        of Integer := ...;'' then it makes sense to also allow ``X: constant
        array(Integer range <>) of Integer := ...;''.  (Note that if
        anonymous array types are ever sensible, a common situation is for a
        table implemented as an array.  Tables are often constant, and for
        constants, there's usually no point in forcing the user to count the
        number of elements in the value.)

                         Wording Changes From Ada 83

        33.d   We have moved the syntax for object_declarations into this
        subclause.

        33.e   Deferred constants no longer have a separate syntax rule, but
        rather are incorporated in object_declaration as constants declared
        without an initialization expression.



3.3.2 Number Declarations

1   A number_declaration declares a named number.

        1.a   Discussion:  {static} If a value or other property of a
        construct is required to be static that means it is required to be
        determined prior to execution.  A static expression is an expression
        whose value is computed at compile time and is usable in contexts
        where the actual value might affect the legality of the construct.
        This is fully defined in clause 4.9.


                                   Syntax

2   number_declaration ::=
         defining_identifier_list : constant := static_expression;


                            Name Resolution Rules

3   {expected type [number_declaration expression]} The static_expression
given for a number_declaration is expected to be of any numeric type.


                               Legality Rules

4   The static_expression given for a number declaration shall be a static
expression, as defined by clause 4.9.


                              Static Semantics

5   The named number denotes a value of type universal_integer if the type of
the static_expression is an integer type.  The named number denotes a value
of type universal_real if the type of the static_expression is a real type.

6   The value denoted by the named number is the value of the
static_expression, converted to the corresponding universal type.  {implicit
subtype conversion [named number value]}


                              Dynamic Semantics

7   {elaboration [number_declaration]} The elaboration of a number_
declaration has no effect.

        7.a   Proof:  Since the static_expression was evaluated at compile
        time.


                                  Examples

8   Examples of number declarations:

9   Two_Pi        : constant := 2.0*Ada.Numerics.Pi;   -- a real number (see A.\
5)

10  Max           : constant := 500;                   -- an integer number
    Max_Line_Size : constant := Max/6                  -- the integer 83
    Power_16      : constant := 2**16;                 -- the integer 65_536
    One, Un, Eins : constant := 1;                     -- three different names\
 for 1


                            Extensions to Ada 83

        10.a   {extensions to Ada 83} We now allow a static expression of any
        numeric type to initialize a named number.  For integer types, it was
        possible in Ada 83 to use 'Pos to define a named number, but there
        was no way to use a static expression of some non-universal real type
        to define a named number.  This change is upward compatible because
        of the preference rule for the operators of the root numeric types.

                         Wording Changes From Ada 83

        10.b   We have moved the syntax rule into this subclause.

        10.c   AI-00263 describes the elaboration of a number declaration in
        words similar to that of an object_declaration.  However, since there
        is no expression to be evaluated and no object to be created, it
        seems simpler to say that the elaboration has no effect.



3.4 Derived Types and Classes

1   {derived type} A derived_type_definition defines a new type (and its
first subtype) whose characteristics are derived from those of a parent type.

        1.a   Glossary entry:  {Derived type} A derived type is a type
        defined in terms of another type, which is the parent type of the
        derived type.  Each class containing the parent type also contains
        the derived type.  The derived type inherits properties such as
        components and primitive operations from the parent.  A type together
        with the types derived from it (directly or indirectly) form a
        derivation class.

{inheritance: see derived types and classes}


                                   Syntax

2   derived_type_definition ::= [abstract] new parent_subtype_indication [recor\
d_extension_part]


                               Legality Rules
3   {parent subtype} {parent type} The parent_subtype_indication defines the
parent subtype; its type is the parent type.

4   A type shall be completely defined (see 3.11.1) prior to being specified
as the parent type in a derived_type_definition -- [the full_type_
declarations for the parent type and any of its subcomponents have to precede
the derived_type_definition.]

        4.a   Discussion:  This restriction does not apply to the ancestor
        type of a private extension -- see 7.3; such a type need not be
        completely defined prior to the private_extension_declaration.
        However, the restriction does apply to record extensions, so the
        ancestor type will have to be completely defined prior to the full_
        type_declaration corresponding to the private_extension_declaration.

        4.b   Reason:  We originally hoped we could relax this restriction.
        However, we found it too complex to specify the rules for a type
        derived from an incompletely defined limited type that subsequently
        became nonlimited.

5   {record extension} If there is a record_extension_part, the derived type
is called a record extension of the parent type.  A record_extension_part
shall be provided if and only if the parent type is a tagged type.

        5.a   Implementation Note:  We allow a record extension to inherit
        discriminants; a previous version of Ada 9X did not.  If the parent
        subtype is unconstrained, it can be implemented as though its
        discriminants were repeated in a new known_discriminant_part and then
        used to constrain the old ones one-for-one.  However, in an extension
        aggregate, the discriminants in this case do not appear in the
        component association list.

        5.b   Ramification:  This rule needs to be rechecked in the visible
        part of an instance of a generic unit.


                              Static Semantics

6   {constrained (subtype)} {unconstrained (subtype)} The first subtype of
the derived type is unconstrained if a known_discriminant_part is provided in
the declaration of the derived type, or if the parent subtype is
unconstrained.  {corresponding constraint} Otherwise, the constraint of the
first subtype corresponds to that of the parent subtype in the following
sense: it is the same as that of the parent subtype except that for a range
constraint (implicit or explicit), the value of each bound of its range is
replaced by the corresponding value of the derived type.

        6.a   Discussion:  A digits_constraint in a subtype_indication for a
        decimal fixed point subtype always imposes a range constraint,
        implicitly if there is no explicit one given.  See 3.5.9, ``Fixed
        Point Types''.

7   The characteristics of the derived type are defined as follows:

    8  Each class of types that includes the parent type also includes
       the derived type.

 8.a    Discussion:  This is inherent in our notion of a ``class'' of
        types.  It is not mentioned in the initial definition of
        ``class'' since at that point type derivation has not been
        defined.  In any case, this rule ensures that every class of
        types is closed under derivation.

    9  If the parent type is an elementary type or an array type, then
       the set of possible values of the derived type is a copy of the
       set of possible values of the parent type.  For a scalar type,
       the base range of the derived type is the same as that of the
       parent type.

 9.a    Discussion:  The base range of a type defined by an integer_
        type_definition or a real_type_definition is determined by the
        _definition, and is not necessarily the same as that of the
        corresponding root numeric type from which the newly defined
        type is implicitly derived.  Treating numerics types as
        implicitly derived from one of the two root numeric types is
        simply to link them into a type hierarchy; such an implicit
        derivation does not follow all the rules given here for an
        explicit derived_type_definition.

   10  If the parent type is a composite type other than an array type,
       then the components, protected subprograms, and entries that are
       declared for the derived type are as follows:

          11  The discriminants specified by a new known_discriminant_
              part, if there is one; otherwise, each discriminant of the
              parent type (implicitly declared in the same order with
              the same specifications) -- {inherited discriminant}
              {inherited component} in the latter case, the dis-
              criminants are said to be inherited, or if unknown in the
              parent, are also unknown in the derived type;

          12  Each nondiscriminant component, entry, and protected
              subprogram of the parent type, implicitly declared in the
              same order with the same declarations; {inherited
              component} {inherited protected subprogram} {inherited
              entry} these components, entries, and protected sub-
              programs are said to be inherited;

 12.a   Ramification:  The profiles of entries and protected subprograms
        do not change upon type derivation, although the type of the
        ``implicit'' parameter identified by the prefix of the name in a
        call does.

 12.b   To be honest:  Any name in the parent type_declaration that
        denotes the current instance of the type is replaced with a name
        denoting the current instance of the derived type, converted to
        the parent type.  {94-4535.d} {94-4537.b}

          13  Each component declared in a record_extension_part, if
              any.

       14   Declarations of components, protected subprograms, and
       entries, whether implicit or explicit, occur immediately within
       the declarative region of the type, in the order indicated above,
       following the parent subtype_indication.

        14.a   Discussion:  The order of declarations within the region
        matters for record_aggregates and extension_aggregates.

        14.b   Ramification:  In most cases, these things are implicitly
        declared immediately following the parent subtype_indication.
        However, 7.3.1, ``Private Operations'' defines some cases in
        which they are implicitly declared later, and some cases in
        which the are not declared at all.

        14.c   Discussion:  The place of the implicit declarations of
        inherited components matters for visibility -- they are not
        visible in the known_discriminant_part nor in the parent
        subtype_indication, but are usually visible within the record_
        extension_part, if any (although there are restrictions on their
        use).  Note that a discriminant specified in a new known_
        discriminant_part is not considered ``inherited'' even if it has
        the same name and subtype as a discriminant of the parent type.

   15  The derived type is limited if and only if the parent type is
       limited.

 15.a   To be honest:  The derived type can become nonlimited if the
        derivation takes place in the visible part of a child package,
        and the parent type is nonlimited as viewed from the private
        part of the child package -- see 7.5.

   16  [For each predefined operator of the parent type, there is a
       corresponding predefined operator of the derived type.]

 16.a   Proof:  This is a ramification of the fact that each class that
        includes the parent type also includes the derived type, and the
        fact that the set of predefined operators that is defined for a
        type, as described in 4.5, is determined by the classes to which
        it belongs.

 16.b   Reason:  Predefined operators are handled separately because
        they follow a slightly different rule than user-defined
        primitive subprograms.  In particular the systematic replacement
        described below does not apply fully to the relational operators
        for Boolean and the exponentiation operator for Integer.  The
        relational operators for a type derived from Boolean still
        return Standard.Boolean.  The exponentiation operator for a type
        derived from Integer still expects Standard.Integer for the
        right operand.  In addition, predefined operators "reemerge"
        when a type is the actual type corresponding to a generic formal
        type, so they need to be well defined even if hidden by
        user-defined primitive subprograms.

   17  {inherited subprogram} For each user-defined primitive subprogram
       (other than a user-defined equality operator -- see below) of the
       parent type that already exists at the place of the derived_type_
       definition, there exists a corresponding inherited primitive
       subprogram of the derived type with the same defining name.
       {equality operator (special inheritance rule for tagged types)}
       Primitive user-defined equality operators of the parent type are
       also inherited by the derived type, except when the derived type
       is a nonlimited record extension, and the inherited operator
       would have a profile that is type conformant with the profile of
       the corresponding predefined equality operator; in this case, the
       user-defined equality operator is not inherited, but is rather
       incorporated into the implementation of the predefined equality
       operator of the record extension (see 4.5.2).  {type conformance
       [partial]}

        17.a   Ramification:  We say ``...already exists...'' rather
        than ``is visible'' or ``has been declared'' because there are
        certain operations that are declared later, but still exist at
        the place of the derived_type_definition, and there are
        operations that are never declared, but still exist.  These
        cases are explained in 7.3.1.

        17.b   Note that nonprivate extensions can appear only after the
        last primitive subprogram of the parent -- the freezing rules
        ensure this.

        17.c   Reason:  A special case is made for the equality
        operators on nonlimited record extensions because their
        predefined equality operators are already defined in terms of
        the primitive equality operator of their parent type (and of the
        tagged components of the extension part).  Inheriting the
        parent's equality operator as is would be undesirable, because
        it would ignore any components of the extension part.  On the
        other hand, if the parent type is limited, then any user-defined
        equality operator is inherited as is, since there is no
        predefined equality operator to take its place.

        17.d   Ramification:  Because user-defined equality operators
        are not inherited by record extensions, the formal parameter
        names of = and /= revert to Left and Right, even if different
        formal parameter names were used in the user-defined equality
        operators of the parent type.

       18   The profile of an inherited subprogram (including an
       inherited enumeration literal) is obtained from the profile of
       the corresponding (user-defined) primitive subprogram of the
       parent type, after systematic replacement of each subtype of its
       profile (see 6.1) that is of the parent type with a corresponding
       subtype of the derived type.  {corresponding subtype} For a given
       subtype of the parent type, the corresponding subtype of the
       derived type is defined as follows:

          19  If the declaration of the derived type has neither a
              known_discriminant_part nor a record_extension_part, then
              the corresponding subtype has a constraint that
              corresponds (as defined above for the first subtype of the
              derived type) to that of the given subtype.

          20  If the derived type is a record extension, then the
              corresponding subtype is the first subtype of the derived
              type.

          21  If the derived type has a new known_discriminant_part but
              is not a record extension, then the corresponding subtype
              is constrained to those values that when converted to the
              parent type belong to the given subtype (see 4.6).
              {implicit subtype conversion [derived type discriminants]}

 21.a   Reason:  An inherited subprogram of an untagged type has an
        Intrinsic calling convention, which precludes the use of the
        Access attribute.  We preclude 'Access because correctly
        performing all required constraint checks on an indirect call to
        such an inherited subprogram was felt to impose an undesirable
        implementation burden.

       22   The same formal parameters have default_expressions in the
       profile of the inherited subprogram.  [Any type mismatch due to
       the systematic replacement of the parent type by the derived type
       is handled as part of the normal type conversion associated with
       parameter passing -- see 6.4.1.]

        22.a   Reason:  We don't introduce the type conversion
        explicitly here since conversions to record extensions or on
        access parameters are not generally legal.  Furthermore, any
        type conversion would just be "undone" since the parent's
        subprogram is ultimately being called anyway.

23   If a primitive subprogram of the parent type is visible at the place of
the derived_type_definition, then the corresponding inherited subprogram is
implicitly declared immediately after the derived_type_definition.  Other-
wise, the inherited subprogram is implicitly declared later or not at all, as
explained in 7.3.1.

24   {derived type [partial]} A derived type can also be defined by a
private_extension_declaration (see 7.3) or a formal_derived_type_definition
(see 12.5.1).  Such a derived type is a partial view of the corresponding
full or actual type.

25   All numeric types are derived types, in that they are implicitly derived
from a corresponding root numeric type (see 3.5.4 and 3.5.6).


                              Dynamic Semantics

26   {elaboration [derived_type_definition]} The elaboration of a derived_
type_definition creates the derived type and its first subtype, and consists
of the elaboration of the subtype_indication and the record_extension_part,
if any.  If the subtype_indication depends on a discriminant, then only those
expressions that do not depend on a discriminant are evaluated.  {94-4535.c}

27   {execution [call on an inherited subprogram]} For the execution of a
call on an inherited subprogram, a call on the corresponding primitive
subprogram of the parent type is performed; the normal conversion of each
actual parameter to the subtype of the corresponding formal parameter (see
6.4.1) performs any necessary type conversion as well.  If the result type of
the inherited subprogram is the derived type, the result of calling the
parent's subprogram is converted to the derived type.  {implicit subtype
conversion [result of inherited function]}

        27.a   Discussion:  If an inherited function returns the derived
        type, and the type is a record extension, then the inherited function
        is abstract, and (unless overridden) cannot be called except via a
        dispatching call.  See 3.9.3.


     NOTES
28   (10) {closed under derivation} Classes are closed under derivation --
     any class that contains a type also contains its derivatives.
     Operations available for a given class of types are available for the
     derived types in that class.

29   (11) Evaluating an inherited enumeration literal is equivalent to
     evaluating the corresponding enumeration literal of the parent type, and
     then converting the result to the derived type.  This follows from their
     equivalence to parameterless functions.  {implicit subtype conversion
     [inherited enumeration literal]}

30   (12) A generic subprogram is not a subprogram, and hence cannot be a
     primitive subprogram and cannot be inherited by a derived type.  On the
     other hand, an instance of a generic subprogram can be a primitive
     subprogram, and hence can be inherited.

31   (13) If the parent type is an access type, then the parent and the
     derived type share the same storage pool; there is a null access value
     for the derived type and it is the implicit initial value for the type.
     See 3.10.

32   (14) If the parent type is a boolean type, the predefined relational
     operators of the derived type deliver a result of the predefined type
     Boolean (see 4.5.2).  If the parent type is an integer type, the right
     operand of the predefined exponentiation operator is of the predefined
     type Integer (see 4.5.6).

33   (15) Any discriminants of the parent type are either all inherited, or
     completely replaced with a new set of discriminants.

34   (16) For an inherited subprogram, the subtype of a formal parameter of
     the derived type need not have any value in common with the first
     subtype of the derived type.

   34.a   Proof:  This happens when the parent subtype is constrained to a
        range that does not overlap with the range of a subtype of the parent
        type that appears in the profile of some primitive subprogram of the
        parent type.  For example:

34.b        type T1 is range 1..100;
            subtype S1 is T1 range 1..10;
            procedure P(X : in S1);  -- P is a primitive subprogram
            type T2 is new T1 range 11..20;
            -- implicitly declared:
            -- procedure P(X : in T2'Base range 1..10);
            --      X cannot be in T2'First .. T2'Last

35   (17) If the reserved word abstract is given in the declaration of a
     type, the type is abstract (see 3.9.3).


                                  Examples

36   Examples of derived type declarations:

37  type Local_Coordinate is new Coordinate;   --  two different types
    type Midweek is new Day range Tue .. Thu;  --  see 3.5.1
    type Counter is new Positive;              --  same range as Positive

38  type Special_Key is new Key_Manager.Key;   --  see 7.3.1
      -- the inherited subprograms have the following specifications:
      --         procedure Get_Key(K : out Special_Key);
      --         function "<"(X,Y : Special_Key) return Boolean;


                         Inconsistencies With Ada 83

        38.a   {inconsistencies with Ada 83} When deriving from a
        (nonprivate, nonderived) type in the same visible part in which it is
        defined, if a predefined operator had been overridden prior to the
        derivation, the derived type will inherit the user-defined operator
        rather than the predefined operator.  The work-around (if the new
        behavior is not the desired behavior) is to move the definition of
        the derived type prior to the overriding of any predefined operators.

                        Incompatibilities With Ada 83

        38.b   {incompatibilities with Ada 83} When deriving from a
        (nonprivate, nonderived) type in the same visible part in which it is
        defined, a primitive subprogram of the parent type declared before
        the derived type will be inherited by the derived type.  This can
        cause upward incompatibilities in cases like this:

38.c           package P is
                  type T is (A, B, C, D);
                  function F( X : T := A ) return Integer;
                  type NT is new T;
                  -- inherits F as
                  -- function F( X : NT := A ) return Integer;
                  -- in Ada 9X only
                  ...
               end P;
               ...
               use P;  -- Only one declaration of F from P is use-visible in
                       -- Ada 83;  two declarations of F are use-visible in
                       -- Ada 9X.
            begin
               ...
               if F > 1 then ... -- legal in Ada 83, ambiguous in Ada 9X

                            Extensions to Ada 83

        38.d   {extensions to Ada 83} The syntax for a derived_type_
        definition is amended to include an optional record_extension_part
        (see 3.9.1).

        38.e   A derived type may override the discriminants of the parent by
        giving a new discriminant_part.  {94-4535.a}

        38.f   The parent type in a derived_type_definition may be a derived
        type defined in the same visible part.

        38.g   When deriving from a type in the same visible part in which it
        is defined, the primitive subprograms declared prior to the
        derivation are inherited as primitive subprograms of the derived
        type.  See 3.2.3.

                         Wording Changes From Ada 83

        38.h   We now talk about the classes to which a type belongs, rather
        than a single class.

        38.i   As explained in Section 13, the concept of "storage pool"
        replaces the Ada 83 concept of "collection."  These concepts are
        similar, but not the same.



3.4.1 Derivation Classes

1   In addition to the various language-defined classes of types, types can
be grouped into derivation classes.


                              Static Semantics

2   {derived from (directly or indirectly)} A derived type is derived from
its parent type directly; it is derived indirectly from any type from which
its parent type is derived.  {derivation class (for a type)} {root type (of a
class)} {rooted at a type} The derivation class of types for a type T (also
called the class rooted at T) is the set consisting of T (the root type of
the class) and all types derived from T (directly or indirectly) plus any
associated universal or class-wide types (defined below).

        2.a   Discussion:  Note that the definition of ``derived from'' is a
        recursive definition.  We don't define a root type for all
        interesting language-defined classes, though presumably we could.

        2.b   To be honest:  By the class-wide type ``associated'' with a
        type T, we mean the type T'Class.  Similarly, the universal type
        associated with root_integer, root_real, and root_fixed are
        universal_integer, universal_real, and universal_fixed, respectively.

3   Every type is either a specific type, a class-wide type, or a universal
type.  {specific type} A specific type is one defined by a type_declaration,
a formal_type_declaration, or a full type definition embedded in a
declaration for an object.  Class-wide and universal types are implicitly
defined, to act as representatives for an entire class of types, as follows:

        3.a   To be honest:  The root types root_integer, root_real, and
        root_fixed are also specific types.  They are declared in the
        specification of package Standard.

4   {class-wide type} Class-wide types
                Class-wide types are defined for [(and belong to)] each
                derivation class rooted at a tagged type (see 3.9).  Given a
                subtype S of a tagged type T, S'Class is the subtype_mark for
                a corresponding subtype of the tagged class-wide type
                T'Class.  Such types are called ``class-wide'' because when a
                formal parameter is defined to be of a class-wide type
                T'Class, an actual parameter of any type in the derivation
                class rooted at T is acceptable (see 8.6).

                5   {first subtype} The set of values for a class-wide type
                T'Class is the discriminated union of the set of values of
                each specific type in the derivation class rooted at T (the
                tag acts as the implicit discriminant -- see 3.9).
                Class-wide types have no primitive subprograms of their own.
                However, as explained in 3.9.2, operands of a class-wide type
                T'Class can be used as part of a dispatching call on a
                primitive subprogram of the type T.  The only components
                [(including discriminants)] of T'Class that are visible are
                those of T.  If S is a first subtype, then S'Class is a first
                subtype.

        5.a   Reason:  We want S'Class to be a first subtype when S is, so
        that an attribute_definition_clause like ``for S'Class'Output use
        ...;'' will be legal.

6   {universal type} Universal types
                Universal types are defined for [(and belong to)] the
                integer, real, and fixed point classes, and are referred to
                in this standard as respectively, universal_integer,
                universal_real, and universal_fixed.  These are analogous to
                class-wide types for these language-defined numeric classes.
                As with class-wide types, if a formal parameter is of a
                universal type, then an actual parameter of any type in the
                corresponding class is acceptable.  In addition, a value of a
                universal type (including an integer or real numeric_literal)
                is ``universal'' in that it is acceptable where some
                particular type in the class is expected (see 8.6).

                7   The set of values of a universal type is the
                undiscriminated union of the set of values possible for any
                definable type in the associated class.  Like class-wide
                types, universal types have no primitive subprograms of their
                own.  However, their ``universality'' allows them to be used
                as operands with the primitive subprograms of any type in the
                corresponding class.

        7.a   Discussion:  A class-wide type is only class-wide in one
        direction, from specific to class-wide, whereas a universal type is
        class-wide (universal) in both directions, from specific to universal
        and back.

        7.b   We considered defining class-wide or perhaps universal types
        for all derivation classes, not just tagged classes and these three
        numeric classes.  However, this was felt to overly weaken the
        strong-typing model in some situations.  Tagged types preserve strong
        type distinctions thanks to the run-time tag.  Class-wide or
        universal types for untagged types would weaken the compile-time type
        distinctions without providing a compensating run-time-checkable
        distinction.

        7.c   We considered defining standard names for the universal numeric
        types so they could be used in formal parameter specifications.
        However, this was felt to impose an undue implementation burden for
        some implementations.

        7.d   To be honest:  Formally, the set of values of a universal type
        is actually a copy of the undiscriminated union of the values of the
        types in its class.  This is because we want each value to have
        exactly one type, with explicit or implicit conversion needed to go
        between types.  An alternative, consistent model would be to
        associate a class, rather than a particular type, with a value, even
        though any given expression would have a particular type.  In that
        case, implicit type conversions would not generally need to change
        the value, although an associated subtype conversion might need to.

8   {root_integer [partial]} {root_real [partial]} The integer and real
numeric classes each have a specific root type in addition to their universal
type, named respectively root_integer and root_real.

9   {cover (a type)} A class-wide or universal type is said to cover all of
the types in its class.  A specific type covers only itself.

10   {descendant (of a type)} A specific type T2 is defined to be a
descendant of a type T1 if T2 is the same as T1, or if T2 is derived
(directly or indirectly) from T1.  A class-wide type T2'Class is defined to
be a descendant of type T1 if T2 is a descendant of T1.  Similarly, the
universal types are defined to be descendants of the root types of their
classes.  {ancestor (of a type)} If a type T2 is a descendant of a type T1,
then T1 is called an ancestor of T2.  {ultimate ancestor (of a type)}
{ancestor (ultimate)} The ultimate ancestor of a type is the ancestor of the
type that is not a descendant of any other type.

        10.a   Ramification:  A specific type is a descendant of itself.
        Class-wide types are considered descendants of the corresponding
        specific type, and do not have any descendants of their own.

        10.b   A specific type is an ancestor of itself.  The root of a
        derivation class is an ancestor of all types in the class, including
        any class-wide types in the class.

        10.c   Discussion:  The terms root, parent, ancestor, and ultimate
        ancestor are all related.  For example:

         10.d  Each type has at most one parent, and one or more
               ancestor types; each type has exactly one ultimate
               ancestor.  In Ada 83, the term ``parent type'' was
               sometimes used more generally to include any ancestor
               type (e.g. RM83-9.4(14)).  In Ada 9X, we restrict parent
               to mean the immediate ancestor.

         10.e  A class of types has at most one root type; a derivation
               class has exactly one root type.

         10.f  The root of a class is an ancestor of all of the types in
               the class (including itself).

         10.g  The type root_integer is the root of the integer class,
               and is the ultimate ancestor of all integer types.  A
               similar statement applies to root_real.

11   {inherited (from an ancestor type)} An inherited component [(including
an inherited discriminant)] of a derived type is inherited from a given
ancestor of the type if the corresponding component was inherited by each
derived type in the chain of derivations going back to the given ancestor.


     NOTES
12   (18) Because operands of a universal type are acceptable to the
     predefined operators of any type in their class, ambiguity can result.
     For universal_integer and universal_real, this potential ambiguity is
     resolved by giving a preference (see 8.6) to the predefined operators of
     the corresponding root types (root_integer and root_real, respectively).
     Hence, in an apparently ambiguous expression like

13       1 + 4 < 7

     14   where each of the literals is of type universal_integer, the
     predefined operators of root_integer will be preferred over those of
     other specific integer types, thereby resolving the ambiguity.

        14.a   Ramification:  Except for this preference, a root numeric type
        is essentially like any other specific type in the associated numeric
        class.  In particular, the result of a predefined operator of a root
        numeric type is not ``universal'' (implicitly convertible) even if
        both operands were.



3.5 Scalar Types

1   {scalar type} Scalar types comprise enumeration types, integer types, and
real types.  {discrete type} Enumeration types and integer types are called
discrete types; {position number} each value of a discrete type has a
position number which is an integer value.  {numeric type} Integer types and
real types are called numeric types.  [All scalar types are ordered, that is,
all relational operators are predefined for their values.]


                                   Syntax

2   range_constraint ::=  range range

3   range ::=  range_attribute_reference
       | simple_expression .. simple_expression


        3.a   Discussion:  These need to be simple_expressions rather than
        more general expressions because ranges appear in membership tests
        and other contexts where expression .. expression would be ambiguous.

4   {range} {lower bound (of a range)} {upper bound (of a range)} {type of a
range} A range has a lower bound and an upper bound and specifies a subset of
the values of some scalar type (the type of the range).  A range with lower
bound L and upper bound R is described by ``L .. R''.  {null range} If R is
less than L, then the range is a null range, and specifies an empty set of
values.  Otherwise, the range specifies the values of the type from the lower
bound to the upper bound, inclusive.  {belong (to a range)} A value belongs
to a range if it is of the type of the range, and is in the subset of values
specified by the range.  {satisfies [a range constraint]} A value satisfies a
range constraint if it belongs to the associated range.  {included (one range
in another)} One range is included in another if all values that belong to
the first range also belong to the second.


                            Name Resolution Rules

5   {expected type [range_constraint range]} For a subtype_indication
containing a range_constraint, either directly or as part of some other
scalar_constraint, the type of the range shall resolve to that of the type
determined by the subtype_mark of the subtype_indication.  {expected type
[range simple_expressions]} For a range of a given type, the simple_
expressions of the range (likewise, the simple_expressions of the equivalent
range for a range_attribute_reference) are expected to be of the type of the
range.

        5.a   Discussion:  In Ada 9X, constraints only appear within subtype_
        indications; things that look like constraints that appear in type
        declarations are called something else like range_specifications.

        5.b   We say "the expected type is ..." or "the type is expected to
        be ..."  depending on which reads better.  They are fundamentally
        equivalent, and both feed into the type resolution rules of clause
        8.6.

        5.c   In some cases, it doesn't work to use expected types.  For
        example, in the above rule, we say that the ``type of the range shall
        resolve to ...''  rather than ``the expected type for the range is
        ...''.  We then use ``expected type'' for the bounds.  If we used
        ``expected'' at both points, there would be an ambiguity, since one
        could apply the rules of 8.6 either on determining the type of the
        range, or on determining the types of the individual bounds.  It is
        clearly important to allow one bound to be of a universal type, and
        the other of a specific type, so we need to use ``expected type'' for
        the bounds.  Hence, we used ``shall resolve to'' for the type of the
        range as a whole.  There are other situations where ``expected type''
        is not quite right, and we use ``shall resolve to'' instead.


                              Static Semantics

6   {base range (of a scalar type) [distributed]} The base range of a scalar
type is the range of finite values of the type that can be represented in
every unconstrained object of the type; it is also the range supported at a
minimum for intermediate values during the evaluation of expressions
involving predefined operators of the type.

        6.a   Implementation Note:  Note that in some machine architectures
        intermediates in an expression (particularly if static), and
        register-resident variables might accommodate a wider range.  The
        base range does not include the values of this wider range that are
        not assignable without overflow to memory-resident objects.

        6.b   Ramification:  {base range [of an enumeration type]} The base
        range of an enumeration type is the range of values of the
        enumeration type.

        6.c   Reason:  If the representation supports infinities, the base
        range is nevertheless restricted to include only the representable
        finite values, so that 'Base'First and 'Base'Last are always
        guaranteed to be finite.

        6.d   To be honest:  By a "value that can be assigned without
        overflow" we don't mean to restrict ourselves to values that can be
        represented exactly.  Values between machine representable values can
        be assigned, but on subsequent reading, a slightly different value
        might be retrieved, as (partially) determined by the number of digits
        of precision of the type.

7   {constrained (subtype)} {unconstrained (subtype)} [A constrained scalar
subtype is one to which a range constraint applies.]  {range (of a scalar
subtype)} The range of a constrained scalar subtype is the range associated
with the range constraint of the subtype.  The range of an unconstrained
scalar subtype is the base range of its type.


                              Dynamic Semantics

8   {compatibility [range with a scalar subtype]} A range is compatible with
a scalar subtype if and only if it is either a null range or each bound of
the range belongs to the range of the subtype.  {compatibility [range_
constraint with a scalar subtype]} A range_constraint is compatible with a
scalar subtype if and only if its range is compatible with the subtype.

        8.a   Ramification:  Only range_constraints (explicit or implicit)
        impose conditions on the values of a scalar subtype.  The other
        scalar_constraints, digit_constraints and delta_constraints impose
        conditions on the subtype denoted by the subtype_mark in a subtype_
        indication, but don't impose a condition on the values of the subtype
        being defined.  Therefore, a scalar subtype is not called constrained
        if all that applies to it is a digits_constraint.  Decimal subtypes
        are subtle, because a digits_constraint without a range_constraint
        nevertheless includes an implicit range_constraint.

9   {elaboration [range_constraint]} The elaboration of a range_constraint
consists of the evaluation of the range.  {evaluation [range]} The evaluation
of a range determines a lower bound and an upper bound.  If simple_
expressions are given to specify bounds, the evaluation of the range
evaluates these simple_expressions in an arbitrary order, and converts them
to the type of the range.  {implicit subtype conversion [bounds of a range]}
If a range_attribute_reference is given, the evaluation of the range consists
of the evaluation of the range_attribute_reference.

10   Attributes

11   For every scalar subtype S, the following attributes are defined:

12  S'First
                S'First denotes the lower bound of the range of S. The value
                of this attribute is of the type of S.

12.a    Ramification:  Evaluating S'First never raises Constraint_Error.

13  S'Last
                S'Last denotes the upper bound of the range of S. The value
                of this attribute is of the type of S.

13.a    Ramification:  Evaluating S'Last never raises Constraint_Error.

14  S'Range
                S'Range is equivalent to the range S'First .. S'Last.

15  {base subtype (of a type)} S'Base
                S'Base denotes an unconstrained subtype of the type of
                S. This unconstrained subtype is called the base subtype of
                the type.

16  S'Min
                S'Min denotes a function with the following specification:

17                  function S'Min(Left, Right : S'Base)
                      return S'Base

                18   The function returns the lesser of the values of the two
                parameters.

18.a    Discussion:  {italics (formal parameters of attribute functions)} The
        formal parameter names are italicized because they cannot be used in
        calls -- see 6.4.  Such a specification cannot be written by the user
        because an attribute_reference is not permitted as the designator of
        a user-defined function, nor can its formal parameters be anonymous.

19  S'Max
                S'Max denotes a function with the following specification:

20                  function S'Max(Left, Right : S'Base)
                      return S'Base

                21   The function returns the greater of the values of the
                two parameters.

22  S'Succ
                S'Succ denotes a function with the following specification:

23                  function S'Succ(Arg : S'Base)
                      return S'Base

                24   {Constraint_Error (raised by failure of run-time check)}
                For an enumeration type, the function returns the value whose
                position number is one more than that of the value of Arg;
                {Range_Check [partial]} {check, language-defined (Range_
                Check)} Constraint_Error is raised if there is no such value
                of the type.  For an integer type, the function returns the
                result of adding one to the value of Arg.  For a fixed point
                type, the function returns the result of adding small to the
                value of Arg.  For a floating point type, the function
                returns the machine number (as defined in 3.5.7) immediately
                above the value of Arg; {Range_Check [partial]} {check,
                language-defined (Range_Check)} Constraint_Error is raised if
                there is no such machine number.

24.a    Ramification:  S'Succ for a modular integer subtype wraps around if
        the value of Arg is S'Base'Last.  S'Succ for a signed integer subtype
        might raise Constraint_Error if the value of Arg is S'Base'Last, or
        it might return the out-of-base-range value S'Base'Last+1, as is
        permitted for all predefined numeric operations.

25  S'Pred
                S'Pred denotes a function with the following specification:

26                  function S'Pred(Arg : S'Base)
                      return S'Base

                27   {Constraint_Error (raised by failure of run-time check)}
                For an enumeration type, the function returns the value whose
                position number is one less than that of the value of Arg;
                {Range_Check [partial]} {check, language-defined (Range_
                Check)} Constraint_Error is raised if there is no such value
                of the type.  For an integer type, the function returns the
                result of subtracting one from the value of Arg.  For a fixed
                point type, the function returns the result of subtracting
                small from the value of Arg.  For a floating point type, the
                function returns the machine number (as defined in 3.5.7)
                immediately below the value of Arg; {Range_Check [partial]}
                {check, language-defined (Range_Check)} Constraint_Error is
                raised if there is no such machine number.

27.a    Ramification:  S'Pred for a modular integer subtype wraps around if
        the value of Arg is S'Base'First.  S'Pred for a signed integer
        subtype might raise Constraint_Error if the value of Arg is
        S'Base'First, or it might return the out-of-base-range value
        S'Base'First-1, as is permitted for all predefined numeric
        operations.

28  S'Wide_Image
                S'Wide_Image denotes a function with the following
                specification:

29                  function S'Wide_Image(Arg : S'Base)
                      return Wide_String

                30   {image (of a value)} The function returns an image of
                the value of Arg, that is, a sequence of characters
                representing the value in display form.  The lower bound of
                the result is one.

                31   The image of an integer value is the corresponding
                decimal literal, without underlines, leading zeros, exponent,
                or trailing spaces, but with a single leading character that
                is either a minus sign or a space.

        31.a   Implementation Note:  If the machine supports negative zeros
        for signed integer types, it is not specified whether "-0" or " 0"
        should be returned for negative zero.  We don't have enough
        experience with such machines to know what is appropriate, and what
        other languages do.  In any case, the implementation should be
        consistent.

                32   {nongraphic character} The image of an enumeration value
                is either the corresponding identifier in upper case or the
                corresponding character literal (including the two
                apostrophes); neither leading nor trailing spaces are
                included.  For a nongraphic character (a value of a character
                type that has no enumeration literal associated with it), the
                result is a corresponding language-defined or implementation-
                defined name in upper case (for example, the image of the
                nongraphic character identified as nul is ``NUL'' -- the
                quotes are not part of the image).

        32.a   Implementation Note:  For an enumeration type T that has
        ``holes'' (caused by an enumeration_representation_clause), {Program_
        Error (raised by failure of run-time check)} T'Wide_Image should
        raise Program_Error if the value is one of the holes (which is a
        bounded error anyway, since holes can be generated only via
        uninitialized variables and similar things.

                33   The image of a floating point value is a decimal real
                literal best approximating the value (rounded away from zero
                if halfway between) with a single leading character that is
                either a minus sign or a space, a single digit (that is
                nonzero unless the value is zero), a decimal point,
                S'Digits-1 (see 3.5.8) digits after the decimal point (but
                one if S'Digits is one), an upper case E, the sign of the
                exponent (either + or -), and two or more digits (with
                leading zeros if necessary) representing the exponent.  If
                S'Signed_Zeros is True, then the leading character is a minus
                sign for a negatively signed zero.  {94-4526.b}

        33.a   To be honest:  Leading zeros are present in the exponent only
        if necessary to make the exponent at least two digits.

        33.b   Reason:  This image is intended to conform to that produced by
        Text_IO.Float_IO.Put in its default format.

        33.c   Implementation Note:  The rounding direction is specified here
        to ensure portability of output results.

                34   The image of a fixed point value is a decimal real
                literal best approximating the value (rounded away from zero
                if halfway between) with a single leading character that is
                either a minus sign or a space, one or more digits before the
                decimal point (with no redundant leading zeros), a decimal
                point, and S'Aft (see 3.5.10) digits after the decimal point.

        34.a   Reason:  This image is intended to conform to that produced by
        Text_IO.Fixed_IO.Put.

        34.b   Implementation Note:  The rounding direction is specified here
        to ensure portability of output results.

        34.c   Implementation Note:  For a machine that supports negative
        zeros, it is not specified whether "-0.000" or " 0.000" is returned.
        See corresponding comment above about integer types with signed
        zeros.

35  S'Image
                S'Image denotes a function with the following specification:

36                  function S'Image(Arg : S'Base)
                      return String

                37   The function returns an image of the value of Arg as a
                String.  The lower bound of the result is one.  The image has
                the same sequence of graphic characters as that defined for
                S'Wide_Image if all the graphic characters are defined in
                Character; otherwise the sequence of characters is
                implementation defined (but no shorter than that of S'Wide_
                Image for the same value of Arg).

        37.a   Implementation defined:  The sequence of characters of the
        value returned by S'Image when some of the graphic characters of
        S'Wide_Image are not defined in Character.

38  S'Wide_Width
                S'Wide_Width denotes the maximum length of a Wide_String
                returned by S'Wide_Image over all values of the subtype S. It
                denotes zero for a subtype that has a null range.  Its type
                is universal_integer.

38.a    Change:  Added Wide_Width attribute as per WG9 resolution.

39  S'Width
                S'Width denotes the maximum length of a String returned by
                S'Image over all values of the subtype S. It denotes zero for
                a subtype that has a null range.  Its type is universal_
                integer.

40  S'Wide_Value
                S'Wide_Value denotes a function with the following
                specification:

41                  function S'Wide_Value(Arg : Wide_String)
                      return S'Base

                42   This function returns a value given an image of the
                value as a Wide_String, ignoring any leading or trailing
                spaces.

                43   {evaluation [Wide_Value]} {Constraint_Error (raised by
                failure of run-time check)} For the evaluation of a call on
                S'Wide_Value for an enumeration subtype S, if the sequence of
                characters of the parameter (ignoring leading and trailing
                spaces) has the syntax of an enumeration literal and if it
                corresponds to a literal of the type of S (or corresponds to
                the result of S'Wide_Image for a nongraphic character of the
                type), the result is the corresponding enumeration value;
                {Range_Check [partial]} {check, language-defined (Range_
                Check)} otherwise Constraint_Error is raised.

        43.a   Discussion:  It's not crystal clear that Range_Check is
        appropriate here, but it doesn't seem worthwhile to invent a whole
        new check name just for this weird case, so we decided to lump it in
        with Range_Check.

                44   {Constraint_Error (raised by failure of run-time check)}
                For the evaluation of a call on S'Wide_Value (or S'Value) for
                an integer subtype S, if the sequence of characters of the
                parameter (ignoring leading and trailing spaces) has the
                syntax of an integer literal, with an optional leading sign
                character (plus or minus for a signed type; only plus for a
                modular type), and the corresponding numeric value belongs to
                the base range of the type of S, then that value is the
                result; {Range_Check [partial]} {check, language-defined
                (Range_Check)} otherwise Constraint_Error is raised.

        44.a   Change:  Changed the syntax accepted by Wide_Value for modular
        types to match Modular_IO.Get; the intent is that these be the same.
        In particular, the number can have a plus sign or no sign; it cannot
        have a minus sign.

        44.b   Discussion:  We considered allowing 'Value to return a
        representable but out-of-range value without a Constraint_Error.
        However, we currently require (see 4.9) in an assignment_statement
        like "X := <numeric_literal>;" that the value of the numeric-literal
        be in X's base range (at compile time), so it seems unfriendly and
        confusing to have a different range allowed for 'Value.  Furthermore,
        for modular types, without the requirement for being in the base
        range, 'Value would have to handle arbitrarily long literals (since
        overflow never occurs for modular types).

                45   For the evaluation of a call on S'Wide_Value (or
                S'Value) for a real subtype S, if the sequence of characters
                of the parameter (ignoring leading and trailing spaces) has
                the syntax of one of the following:

                   46  numeric_literal

                   47  numeral.[exponent]

                   48  .numeral[exponent]

                   49  base#based_numeral.#[exponent]

                   50  base#.based_numeral#[exponent]

                51   {Constraint_Error (raised by failure of run-time check)}
                with an optional leading sign character (plus or minus), and
                if the corresponding numeric value belongs to the base range
                of the type of S, then that value is the result; {Range_Check
                [partial]} {check, language-defined (Range_Check)} otherwise
                Constraint_Error is raised.  The sign of a zero value is
                preserved (positive if none has been specified) if S'Signed_
                Zeros is True.  {94-4526.b}

52  S'Value
                S'Value denotes a function with the following specification:

53                  function S'Value(Arg : String)
                      return S'Base

                54   This function returns a value given an image of the
                value as a String, ignoring any leading or trailing spaces.

                55   {evaluation [Value]} {Constraint_Error (raised by
                failure of run-time check)} For the evaluation of a call on
                S'Value for an enumeration subtype S, if the sequence of
                characters of the parameter (ignoring leading and trailing
                spaces) has the syntax of an enumeration literal and if it
                corresponds to a literal of the type of S (or corresponds to
                the result of S'Image for a value of the type), the result is
                the corresponding enumeration value; {Range_Check [partial]}
                {check, language-defined (Range_Check)} otherwise Constraint_
                Error is raised.  For a numeric subtype S, the evaluation of
                a call on S'Value with Arg of type String is equivalent to a
                call on S'Wide_Value for a corresponding Arg of type Wide_
                String.

        55.a   Reason:  S'Value is subtly different from S'Wide_Value for
        enumeration subtypes since S'Image might produce a different sequence
        of characters than S'Wide_Image if the enumeration literal uses
        characters outside of the predefined type Character.  That is why we
        don't just define S'Value in terms of S'Wide_Value for enumeration
        subtypes.  S'Value and S'Wide_Value for numeric subtypes yield the
        same result given the same sequence of characters.


                         Implementation Permissions

56   An implementation may extend the Wide_Value, [Value, Wide_Image, and
Image] attributes of a floating point type to support special values such as
infinities and NaNs.  {94-4526.c} {94-4893.d} {94-4901.a}

        56.a   Proof:  The permission is really only necessary for Wide_
        Value, because Value is defined in terms of Wide_Value, and because
        the behavior of Wide_Image and Image is already unspecified for
        things like infinities and NaNs.

        56.b   Reason:  This is to allow implementations to define full
        support for IEEE arithmetic.  See also the similar permission for Get
        in A.10.9.


     NOTES
57   (19) The evaluation of S'First or S'Last never raises an exception.  If
     a scalar subtype S has a nonnull range, S'First and S'Last belong to
     this range.  These values can, for example, always be assigned to a
     variable of subtype S.

   57.a   Discussion:  This paragraph addresses an issue that came up with
        Ada 83, where for fixed point types, the end points of the range
        specified in the type definition were not necessarily within the base
        range of the type.  However, it was later clarified (and we reconfirm
        it in 3.5.9, ``Fixed Point Types'') that the First and Last
        attributes reflect the true bounds chosen for the type, not the
        bounds specified in the type definition (which might be outside the
        ultimately chosen base range).

58   (20) For a subtype of a scalar type, the result delivered by the
     attributes Succ, Pred, and Value might not belong to the subtype;
     similarly, the actual parameters of the attributes Succ, Pred, and Image
     need not belong to the subtype.

59   (21) For any value V (including any nongraphic character) of an
     enumeration subtype S, S'Value(S'Image(V)) equals V, as does S'Wide_
     Value(S'Wide_Image(V)).  Neither expression ever raises Constraint_
     Error.


                                  Examples

60   Examples of ranges:

61  -10 .. 10
    X .. X + 1
    0.0 .. 2.0*Pi
    Red .. Green     -- see 3.5.1
    1 .. 0           -- a null range
    Table'Range      -- a range attribute reference (see 3.6)

62   Examples of range constraints:

63  range -999.0 .. +999.0
    range S'First+1 .. S'Last-1


                        Incompatibilities With Ada 83

        63.a   {incompatibilities with Ada 83} S'Base is no longer defined
        for nonscalar types.  One conceivable existing use of S'Base for
        nonscalar types is S'Base'Size where S is a generic formal private
        type.  However, that is not generally useful because the actual
        subtype corresponding to S might be a constrained array or
        discriminated type, which would mean that S'Base'Size might very well
        overflow (for example, S'Base'Size where S is a constrained subtype
        of String will generally be 8 * (Integer'Last + 1)).  For derived
        discriminated types that are packed, S'Base'Size might not even be
        well defined if the first subtype is constrained, thereby allowing
        some amount of normally required ``dope'' to have been squeezed out
        in the packing.  Hence our conclusion is that S'Base'Size is not
        generally useful in a generic, and does not justify keeping the
        attribute Base for nonscalar types just so it can be used as a
        prefix.

                            Extensions to Ada 83

        63.b   {extensions to Ada 83} The attribute S'Base for a scalar
        subtype is now permitted anywhere a subtype_mark is permitted.
        S'Base'First .. S'Base'Last is the base range of the type.  Using an
        attribute_definition_clause, one cannot specify any subtype-specific
        attributes for the subtype denoted by S'Base (the base subtype).

        63.c   The attribute S'Range is now allowed for scalar subtypes.

        63.d   The attributes S'Min and S'Max are now defined, and made
        available for all scalar types.

        63.e   The attributes S'Succ, S'Pred, S'Image, S'Value, and S'Width
        are now defined for real types as well as discrete types.

        63.f   Wide_String versions of S'Image and S'Value are defined.
        These are called S'Wide_Image and S'Wide_Value to avoid introducing
        ambiguities involving uses of these attributes with string literals.

                         Wording Changes From Ada 83

        63.g   We now use the syntactic category range_attribute_reference
        since it is now syntactically distinguished from other attribute
        references.

        63.h   The definition of S'Base has been moved here from 3.3.3 since
        it now applies only to scalar types.

        63.i   More explicit rules are provided for nongraphic characters.



3.5.1 Enumeration Types

1   [{enumeration type} An enumeration_type_definition defines an enumeration
type.]


                                   Syntax

2   enumeration_type_definition ::=
       (enumeration_literal_specification {, enumeration_literal_specification})

3   enumeration_literal_specification ::=  defining_identifier | defining_chara\
cter_literal

4   defining_character_literal ::= character_literal


                               Legality Rules

5   [The defining_identifiers and defining_character_literals listed in an
enumeration_type_definition shall be distinct.]

        5.a   Proof:  This is a ramification of the normal disallowance of
        homographs explicitly declared immediately in the same declarative
        region.


                              Static Semantics
6   {enumeration literal} Each enumeration_literal_specification is the
explicit declaration of the corresponding enumeration literal: it declares a
parameterless function, whose defining name is the defining_identifier or
defining_character_literal, and whose result type is the enumeration type.

        6.a   Reason:  This rule defines the profile of the enumeration
        literal, which is used in the various types of conformance.

        6.b   Ramification:  The parameterless function associated with an
        enumeration literal is fully defined by the enumeration_type_
        definition; a body is not permitted for it, and it never fails the
        Elaboration_Check when called.

7   Each enumeration literal corresponds to a distinct value of the
enumeration type, and to a distinct position number.  {position number [of an
enumeration value]} The position number of the value of the first listed
enumeration literal is zero; the position number of the value of each
subsequent enumeration literal is one more than that of its predecessor in
the list.

8   [The predefined order relations between values of the enumeration type
follow the order of corresponding position numbers.]

9   [{overloaded [enumeration literal]} If the same defining_identifier or
defining_character_literal is specified in more than one enumeration_type_
definition, the corresponding enumeration literals are said to be overloaded.
At any place where an overloaded enumeration literal occurs in the text of a
program, the type of the enumeration literal has to be determinable from the
context (see 8.6).]


                              Dynamic Semantics

10   {elaboration [enumeration_type_definition]} {constrained (subtype)}
{unconstrained (subtype)} The elaboration of an enumeration_type_definition
creates the enumeration type and its first subtype, which is constrained to
the base range of the type.

        10.a   Ramification:  The first subtype of a discrete type is always
        constrained, except in the case of a derived type whose parent
        subtype is Whatever'Base.

11   When called, the parameterless function associated with an enumeration
literal returns the corresponding value of the enumeration type.


     NOTES
12   (22) If an enumeration literal occurs in a context that does not
     otherwise suffice to determine the type of the literal, then
     qualification by the name of the enumeration type is one way to resolve
     the ambiguity (see 4.7).


                                  Examples

13   Examples of enumeration types and subtypes:

14  type Day    is (Mon, Tue, Wed, Thu, Fri, Sat, Sun);
    type Suit   is (Clubs, Diamonds, Hearts, Spades);
    type Gender is (M, F);
    type Level  is (Low, Medium, Urgent);
    type Color  is (White, Red, Yellow, Green, Blue, Brown, Black);
    type Light  is (Red, Amber, Green); -- Red and Green are overloaded

15  type Hexa   is ('A', 'B', 'C', 'D', 'E', 'F');
    type Mixed  is ('A', 'B', '*', B, None, '?', '%');

16  subtype Weekday is Day   range Mon .. Fri;
    subtype Major   is Suit  range Hearts .. Spades;
    subtype Rainbow is Color range Red .. Blue;  --  the Color Red, not the Lig\
ht


                         Wording Changes From Ada 83

        16.a   The syntax rule for defining_character_literal is new.  It is
        used for the defining occurrence of a character_literal, analogously
        to defining_identifier.  Usage occurrences use the name or selector_
        name syntactic categories.

        16.b   We emphasize the fact that an enumeration literal denotes a
        function, which is called to produce a value.



3.5.2 Character Types

                              Static Semantics

1   {character type} An enumeration type is said to be a character type if at
least one of its enumeration literals is a character_literal.

2   {Latin-1} {BMP} {ISO 10646} {Character} The predefined type Character is
a character type whose values correspond to the 256 code positions of Row 00
(also known as Latin-1) of the ISO 10646 Basic Multilingual Plane (BMP).
Each of the graphic characters of Row 00 of the BMP has a corresponding
character_literal in Character.  Each of the nongraphic positions of Row 00
(0000-001F and 007F-009F) has a corresponding language-defined name, which is
not usable as an enumeration literal, but which is usable with the attributes
(Wide_)Image and (Wide_)Value; these names are given in the definition of
type Character in A.1, ``The Package Standard'', but are set in italics.
{italics (nongraphic characters)}

3   {Wide_Character} {BMP} {ISO 10646} The predefined type Wide_Character is
a character type whose values correspond to the 65536 code positions of the
ISO 10646 Basic Multilingual Plane (BMP).  Each of the graphic characters of
the BMP has a corresponding character_literal in Wide_Character.  The first
256 values of Wide_Character have the same character_literal or
language-defined name as defined for Character.  The last 2 values of Wide_
Character correspond to the nongraphic positions FFFE and FFFF of the BMP,
and are assigned the language-defined names FFFE and FFFF.  As with the other
language-defined names for nongraphic characters, the names FFFE and FFFF are
usable only with the attributes (Wide_)Image and (Wide_)Value; they are not
usable as enumeration literals.  All other values of Wide_Character are
considered graphic characters, and have a corresponding character_literal.

        3.a   Reason:  The language-defined names are not usable as
        enumeration literals to avoid "polluting" the name space.  Since
        Wide_Character is defined in Standard, if the names FFFE and FFFF
        were usable as enumeration literals, they would hide other
        nonoverloadable declarations with the same names in use-d packages.

        3.b   ISO 10646 has not defined the meaning of all of the code
        positions from 0100 through FFFD, but they are all considered graphic
        characters by Ada to simplify the implementation, and to allow for
        revisions to ISO 10646.  In ISO 10646, FFFE and FFFF are special, and
        will never be associated with graphic characters in any revision.


                         Implementation Permissions

4   {localization} In a nonstandard mode, an implementation may provide other
interpretations for the predefined types Character and Wide_Character[, to
conform to local conventions].


                            Implementation Advice

5   {localization} If an implementation supports a mode with alternative
interpretations for Character and Wide_Character, the set of graphic
characters of Character should nevertheless remain a proper subset of the set
of graphic characters of Wide_Character.  Any character set ``localizations''
should be reflected in the results of the subprograms defined in the
language-defined package Characters.Handling (see A.3) available in such a
mode.  In a mode with an alternative interpretation of Character, the
implementation should also support a corresponding change in what is a legal
identifier_letter.


     NOTES
6    (23) The language-defined library package Characters.Latin_1 (see A.3.3)
     includes the declaration of constants denoting control characters, lower
     case characters, and special characters of the predefined type
     Character.

   6.a   To be honest:  The package ASCII does the same, but only for the
        first 128 characters of Character.  Hence, it is an obsolescent
        package, and we no longer mention it here.

7    (24) A conventional character set such as EBCDIC can be declared as a
     character type; the internal codes of the characters can be specified by
     an enumeration_representation_clause as explained in clause 13.4.


                                  Examples

8   Example of a character type:

9   type Roman_Digit is ('I', 'V', 'X', 'L', 'C', 'D', 'M');


                         Inconsistencies With Ada 83

        9.a   {inconsistencies with Ada 83} The declaration of Wide_Character
        in package Standard hides use-visible declarations with the same
        defining identifier.  In the unlikely event that an Ada 83 program
        had depended on such a use-visible declaration, and the program
        remains legal after the substitution of Standard.Wide_Character, the
        meaning of the program will be different.

                        Incompatibilities With Ada 83

        9.b   {incompatibilities with Ada 83} The presence of Wide_Character
        in package Standard means that an expression such as

9.c         'a' = 'b'

        9.d   is ambiguous in Ada 9X, whereas in Ada 83 both literals could
        be resolved to be of type Character.

        9.e   The change in visibility rules (see 4.2) for character literals
        means that additional qualification might be necessary to resolve
        expressions involving overloaded subprograms and character literals.

                            Extensions to Ada 83

        9.f   {extensions to Ada 83} The type Character has been extended to
        have 256 positions, and the type Wide_Character has been added.  Note
        that this change was already approved by the ARG for Ada 83
        conforming compilers.

        9.g   The rules for referencing character literals are changed (see
        4.2), so that the declaration of the character type need not be
        directly visible to use its literals, similar to null and string
        literals.  Context is used to resolve their type.



3.5.3 Boolean Types

                              Static Semantics

1   {Boolean} There is a predefined enumeration type named Boolean, [declared
in the visible part of package Standard].  {False} {True} It has the two
enumeration literals False and True ordered with the relation False < True.
{boolean type} Any descendant of the predefined type Boolean is called a
boolean type.

        1.a   Implementation Note:  An implementation is not required to
        support enumeration representation clauses on boolean types that
        impose an unacceptable implementation burden.  See 13.4,
        ``Enumeration Representation Clauses''.  However, it is generally
        straightforward to support representations where False is zero and
        True is 2**n - 1 for some n.



3.5.4 Integer Types

1   {integer type} {signed integer type} {modular type} An integer_type_
definition defines an integer type; it defines either a signed integer type,
or a modular integer type.  The base range of a signed integer type includes
at least the values of the specified range.  A modular type is an integer
type with all arithmetic modulo a specified positive modulus; such a type
corresponds to an unsigned type with wrap-around semantics.  {unsigned type:
see modular type}


                                   Syntax

2   integer_type_definition ::= signed_integer_type_definition | modular_type_d\
efinition

3   signed_integer_type_definition ::= range static_simple_expression .. static\
_simple_expression

        3.a   Discussion:  We don't call this a range_constraint, because it
        is rather different -- not only is it required to be static, but the
        associated overload resolution rules are different than for normal
        range constraints.  A similar comment applies to real_range_
        specification.  This used to be integer_range_specification but when
        we added support for modular types, it seemed overkill to have three
        levels of syntax rules, and just calling these signed_integer_range_
        specification and modular_range_specification loses the fact that
        they are defining different classes of types, which is important for
        the generic type matching rules.

4   modular_type_definition ::= mod static_expression


                            Name Resolution Rules

5   {expected type [signed_integer_type_definition simple_expression]} Each
simple_expression in a signed_integer_type_definition is expected to be of
any integer type; they need not be of the same type.  {expected type
[modular_type_definition expression]} The expression in a modular_type_
definition is likewise expected to be of any integer type.


                               Legality Rules

6   The simple_expressions of a signed_integer_type_definition shall be
static, and their values shall be in the range System.Min_Int .. System.Max_
Int.

7   {modulus (of a modular type)} {Max_Binary_Modulus} {Max_Nonbinary_
Modulus} The expression of a modular_type_definition shall be static, and its
value (the modulus) shall be positive, and shall be no greater than
System.Max_Binary_Modulus if a power of 2, or no greater than System.Max_
Nonbinary_Modulus if not.

        7.a   Reason:  For a 2's-complement machine, supporting nonbinary
        moduli greater than System.Max_Int can be quite difficult, whereas
        essentially any binary moduli are straightforward to support, up to
        2*System.Max_Int+2, so this justifies having two separate limits.


                              Static Semantics

8   The set of values for a signed integer type is the (infinite) set of
mathematical integers[, though only values of the base range of the type are
fully supported for run-time operations].  The set of values for a modular
integer type are the values from 0 to one less than the modulus, inclusive.

9   {base range [of a signed integer type]} A signed_integer_type_definition
defines an integer type whose base range includes at least the values of the
simple_expressions and is symmetric about zero, excepting possibly an extra
negative value.  {constrained (subtype)} {unconstrained (subtype)} A signed_
integer_type_definition also defines a constrained first subtype of the type,
with a range whose bounds are given by the values of the simple_expressions,
converted to the type being defined.  {implicit subtype conversion [bounds of
signed integer type]}

        9.a   Implementation Note:  The base range of a signed integer type
        might be much larger than is necessary to satisfy the aboved
        requirements.

10   {base range [of a modular type]} A modular_type_definition defines a
modular type whose base range is from zero to one less than the given
modulus.  {constrained (subtype)} {unconstrained (subtype)} A modular_type_
definition also defines a constrained first subtype of the type with a range
that is the same as the base range of the type.

11   {Integer} There is a predefined signed integer subtype named Integer[,
declared in the visible part of package Standard].  It is constrained to the
base range of its type.

        11.a   Reason:  Integer is a constrained subtype, rather than an
        unconstrained subtype.  This means that on assignment to an object of
        subtype Integer, a range check is required.  On the other hand, an
        object of subtype Integer'Base is unconstrained, and no range check
        (only overflow check) is required on assignment.  For example, if the
        object is held in an extended-length register, its value might be
        outside of Integer'First .. Integer'Last.  All parameter and result
        subtypes of the predefined integer operators are of such
        unconstrained subtypes, allowing extended-length registers to be used
        as operands or for the result.  In an earlier version of Ada 9X,
        Integer was unconstrained.  However, the fact that certain
        Constraint_Errors might be omitted or appear elsewhere was felt to be
        an undesirable upward inconsistency in this case.  Note that for
        Float, the opposite conclusion was reached, partly because of the
        high cost of performing range checks when not actually necessary.
        Objects of subtype Float are unconstrained, and no range checks, only
        overflow checks, are performed for them.

12   {Natural} {Positive} Integer has two predefined subtypes, [declared in
the visible part of package Standard:]

13  subtype Natural  is Integer range 0 .. Integer'Last;
    subtype Positive is Integer range 1 .. Integer'Last;

14   {root_integer} {Min_Int} {Max_Int} A type defined by an integer_type_
definition is implicitly derived from root_integer, an anonymous predefined
(specific) integer type, whose base range is System.Min_Int .. System.Max_
Int.  However, the base range of the new type is not inherited from root_
integer, but is instead determined by the range or modulus specified by the
integer_type_definition.  {universal_integer [partial]} {integer literals}
[Integer literals are all of the type universal_integer, the universal type
(see 3.4.1) for the class rooted at root_integer, allowing their use with the
operations of any integer type.]

        14.a   Discussion:  This implicit derivation is not considered
        exactly equivalent to explicit derivation via a derived_type_
        definition.  In particular, integer types defined via a derived_type_
        definition inherit their base range from their parent type.  A type
        defined by an integer_type_definition does not necessarily inherit
        its base range from root_integer.  It is not specified whether the
        implicit derivation from root_integer is direct or indirect, not that
        it really matters.  All we want is for all integer types to be
        descendants of root_integer.

        14.b   Implementation Note:  It is the intent that even nonstandard
        integer types (see below) will be descendants of root_integer, even
        though they might have a base range that exceeds that of root_
        integer.  This causes no problem for static calculations, which are
        performed without range restrictions (see 4.9).  However for run-time
        calculations, it is possible that Constraint_Error might be raised
        when using an operator of root_integer on the result of 'Val applied
        to a value of a nonstandard integer type.

15   {position number [of an integer value]} The position number of an
integer value is equal to the value.

16   For every modular subtype S, the following attribute is defined:

17  S'Modulus
                S'Modulus yields the modulus of the type of S, as a value of
                the type universal_integer.


                              Dynamic Semantics

18   {elaboration [integer_type_definition]} The elaboration of an integer_
type_definition creates the integer type and its first subtype.

19   For a modular type, if the result of the execution of a predefined
operator (see 4.5) is outside the base range of the type, the result is
reduced modulo the modulus of the type to a value that is within the base
range of the type.

20   {Overflow_Check [partial]} {check, language-defined (Overflow_Check)}
{Constraint_Error (raised by failure of run-time check)} For a signed integer
type, the exception Constraint_Error is raised by the execution of an
operation that cannot deliver the correct result because it is outside the
base range of the type.[{Division_Check [partial]} {check, language-defined
(Division_Check)} {Constraint_Error (raised by failure of run-time check)}
For any integer type, Constraint_Error is raised by the operators "/", "rem",
and "mod" if the right operand is zero.]
                         Implementation Requirements

21   {Integer} In an implementation, the range of Integer shall include the
range -2**15+1 .. +2**15-1.

22   {Long_Integer} If Long_Integer is predefined for an implementation, then
its range shall include the range -2**31+1 .. +2**31-1.

23   System.Max_Binary_Modulus shall be at least 2**16.  {94-4776.b}
{94-4789.a} {94-4790.a}


                         Implementation Permissions

24   For the execution of a predefined operation of a signed integer type,
the implementation need not raise Constraint_Error if the result is outside
the base range of the type, so long as the correct result is produced.

        24.a   Discussion:  Constraint_Error is never raised for operations
        on modular types, except for divide-by-zero (and rem/mod-by-zero).

25   {Long_Integer} {Short_Integer} An implementation may provide additional
predefined signed integer types[, declared in the visible part of Standard],
whose first subtypes have names of the form Short_Integer, Long_Integer,
Short_Short_Integer, Long_Long_Integer, etc.  Different predefined integer
types are allowed to have the same base range.  However, the range of Integer
should be no wider than that of Long_Integer.  Similarly, the range of Short_
Integer (if provided) should be no wider than Integer.  Corresponding
recommendations apply to any other predefined integer types.  There need not
be a named integer type corresponding to each distinct base range supported
by an implementation.  The range of each first subtype should be the base
range of its type.

        25.a   Implementation defined:  The predefined integer types declared
        in Standard.

26   {nonstandard integer type} An implementation may provide nonstandard
integer types, descendants of root_integer that are declared outside of the
specification of package Standard, which need not have all the standard
characteristics of a type defined by an integer_type_definition.  For
example, a nonstandard integer type might have an asymmetric base range or it
might not be allowed as an array or loop index (a very long integer).  Any
type descended from a nonstandard integer type is also nonstandard.  An
implementation may place arbitrary restrictions on the use of such types; it
is implementation defined whether operators that are predefined for ``any
integer type'' are defined for a particular nonstandard integer type.  [In
any case, such types are not permitted as explicit_generic_actual_parameters
for formal scalar types -- see 12.5.2.]

        26.a   Implementation defined:  Any nonstandard integer types and the
        operators defined for them.

27   {one's complement [modular types]} For a one's complement machine, the
high bound of the base range of a modular type whose modulus is one less than
a power of 2 may be equal to the modulus, rather than one less than the
modulus.  It is implementation defined for which powers of 2, if any, this
permission is exercised.


                            Implementation Advice

28   {Long_Integer} An implementation should support Long_Integer in addition
to Integer if the target machine supports 32-bit (or longer) arithmetic.  No
other named integer subtypes are recommended for package Standard.  Instead,
appropriate named integer subtypes should be provided in the library package
Interfaces (see B.2).

        28.a   Implementation Note:  To promote portability, implementations
        should explicitly declare the integer (sub)types Integer and Long_
        Integer in Standard, and leave other predefined integer types
        anonymous.  For implementations that already support Byte_Integer,
        etc., upward compatibility argues for keeping such declarations in
        Standard during the transition period, but perhaps generating a
        warning on use.  A separate package Interfaces in the predefined
        environment is available for pre-declaring types such as Integer_8,
        Integer_16, etc.  See B.2.  In any case, if the user declares a
        subtype (first or not) whose range fits in, for example, a byte, the
        implementation can store variables of the subtype in a single byte,
        even if the base range of the type is wider.

29   {two's complement [modular types]} An implementation for a two's
complement machine should support modular types with a binary modulus up to
System.Max_Int*2+2.  An implementation should support a nonbinary modulus up
to Integer'Last.

        29.a   Reason:  Modular types provide bit-wise "and", "or", "xor",
        and "not" operations.  It is important for systems programming that
        these be available for all integer types of the target hardware.

        29.b   Ramification:  Note that on a one's complement machine, the
        largest supported modular type would normally have a nonbinary
        modulus.  On a two's complement machine, the largest supported
        modular type would normally have a binary modulus.

        29.c   Implementation Note:  Supporting a nonbinary modulus greater
        than Integer'Last can impose an undesirable implementation burden on
        some machines.


     NOTES
30   (25) {universal_integer} {integer literals} Integer literals are of the
     anonymous predefined integer type universal_integer.  Other integer
     types have no literals.  However, the overload resolution rules (see
     8.6, ``The Context of Overload Resolution'') allow expressions of the
     type universal_integer whenever an integer type is expected.

31   (26) The same arithmetic operators are predefined for all signed integer
     types defined by a signed_integer_type_definition (see 4.5, ``Operators
     and Expression Evaluation'').  For modular types, these same operators
     are predefined, plus bit-wise logical operators (and, or, xor, and not).
     In addition, for the unsigned types declared in the language-defined
     package Interfaces (see B.2), functions are defined that provide
     bit-wise shifting and rotating.

32   (27) Modular types match a generic_formal_parameter_declaration of the
     form "type T is mod <>;"; signed integer types match "type T is range
     <>;" (see 12.5.2).


                                  Examples

33   Examples of integer types and subtypes:

34  type Page_Num  is range 1 .. 2_000;
    type Line_Size is range 1 .. Max_Line_Size;

35  subtype Small_Int   is Integer   range -10 .. 10;
    subtype Column_Ptr  is Line_Size range 1 .. 10;
    subtype Buffer_Size is Integer   range 0 .. Max;

36  type Byte        is mod 256; -- an unsigned byte
    type Hash_Index  is mod 97;  -- modulus is prime


                            Extensions to Ada 83

        36.a   {extensions to Ada 83} An implementation is allowed to support
        any number of distinct base ranges for integer types, even if fewer
        integer types are explicitly declared in Standard.

        36.b   Modular (unsigned, wrap-around) types are new.

                         Wording Changes From Ada 83

        36.c   Ada 83's integer types are now called "signed" integer types,
        to contrast them with "modular" integer types.

        36.d   Standard.Integer, Standard.Long_Integer, etc., denote con-
        strained subtypes of predefined integer types, consistent with the
        Ada 9X model that only subtypes have names.

        36.e   We now impose minimum requirements on the base range of
        Integer and Long_Integer.

        36.f   We no longer explain integer type definition in terms of an
        equivalence to a normal type derivation, except to say that all
        integer types are by definition implicitly derived from root_integer.
        This is for various reasons.

        36.g   First of all, the equivalence with a type derivation and a
        subtype declaration was not perfect, and was the source of various
        AIs (for example, is the conversion of the bounds static?  Is a
        numeric type a derived type with respect to other rules of the
        language?)

        36.h   Secondly, we don't want to require that every integer size
        supported shall have a corresponding named type in Standard.  Adding
        named types to Standard creates nonportabilities.

        36.i   Thirdly, we don't want the set of types that match a formal
        derived type "type T is new Integer;" to depend on the particular
        underlying integer representation chosen to implement a given
        user-defined integer type.  Hence, we would have needed anonymous
        integer types as parent types for the implicit derivation anyway.  We
        have simply chosen to identify only one anonymous integer type --
        root_integer, and stated that every integer type is derived from it.

        36.j   Finally, the ``fiction'' that there were distinct preexisting
        predefined types for every supported representation breaks down for
        fixed point with arbitrary smalls, and was never exploited for
        enumeration types, array types, etc.  Hence, there seems little
        benefit to pushing an explicit equivalence between integer type
        definition and normal type derivation.



3.5.5 Operations of Discrete Types

                              Static Semantics

1   For every discrete subtype S, the following attributes are defined:

2   S'Pos
                S'Pos denotes a function with the following specification:

3                   function S'Pos(Arg : S'Base)
                      return universal_integer

                4   This function returns the position number of the value of
                Arg, as a value of type universal_integer.

5   S'Val
                S'Val denotes a function with the following specification:

6                   function S'Val(Arg : universal_integer)
                      return S'Base

                7   {evaluation [Val]} {Constraint_Error (raised by failure
                of run-time check)} This function returns a value of the type
                of S whose position number equals the value of Arg.  {Range_
                Check [partial]} {check, language-defined (Range_Check)} For
                the evaluation of a call on S'Val, if there is no value in
                the base range of its type with the given position number,
                Constraint_Error is raised.

7.a     Ramification:  By the overload resolution rules, a formal parameter
        of type universal_integer allows an actual parameter of any integer
        type.

7.b     Reason:  We considered allowing S'Val for a signed integer subtype S
        to return an out-of-range value, but since checks were required for
        enumeration and modular types anyway, the allowance didn't seem worth
        the complexity of the rule.


                            Implementation Advice

8   For the evaluation of a call on S'Pos for an enumeration subtype, if the
value of the operand does not correspond to the internal code for any
enumeration literal of its type [(perhaps due to an uninitialized variable)],
then the implementation should raise Program_Error.  {Program_Error (raised
by failure of run-time check)} This is particularly important for enumeration
types with noncontiguous internal codes specified by an enumeration_
representation_clause.

        8.a   Reason:  We say Program_Error here, rather than Constraint_
        Error, because the main reason for such values is uninitialized
        variables, and the normal way to indicate such a use (if detected) is
        to raise Program_Error.  (Other reasons would involve the misuse of
        low-level features such as Unchecked_Conversion.)


     NOTES
9    (28) Indexing and loop iteration use values of discrete types.

10   (29) {predefined operations [of a discrete type]} The predefined
     operations of a discrete type include the assignment operation,
     qualification, the membership tests, and the relational operators; for a
     boolean type they include the short-circuit control forms and the
     logical operators; for an integer type they include type conversion to
     and from other numeric types, as well as the binary and unary adding
     operators - and +, the multiplying operators, the unary operator abs,
     and the exponentiation operator.  {94-4693.v} The assignment operation
     is described in 5.2.  The other predefined operations are described in
     Section 4.

11   (30) As for all types, objects of a discrete type have Size and Address
     attributes (see 13.3).

12   (31) For a subtype of a discrete type, the result delivered by the
     attribute Val might not belong to the subtype; similarly, the actual
     parameter of the attribute Pos need not belong to the subtype.  The
     following relations are satisfied (in the absence of an exception) by
     these attributes:

13       S'Val(S'Pos(X)) = X
         S'Pos(S'Val(N)) = N


                                  Examples

14   Examples of attributes of discrete subtypes:

15  --  For the types and subtypes declared in subclause 3.5.1 the following ho\
ld:

16  --  Color'First   = White,   Color'Last   = Black
    --  Rainbow'First = Red,     Rainbow'Last = Blue

17  --  Color'Succ(Blue) = Rainbow'Succ(Blue) = Brown
    --  Color'Pos(Blue)  = Rainbow'Pos(Blue)  = 4
    --  Color'Val(0)     = Rainbow'Val(0)     = White


                            Extensions to Ada 83

        17.a   {extensions to Ada 83} The attributes S'Succ, S'Pred, S'Width,
        S'Image, and S'Value have been generalized to apply to real types as
        well (see 3.5, ``Scalar Types'').



3.5.6 Real Types

1   {real type} Real types provide approximations to the real numbers, with
relative bounds on errors for floating point types, and with absolute bounds
for fixed point types.


                                   Syntax

2   real_type_definition ::=
       floating_point_definition | fixed_point_definition


                              Static Semantics

3   {root_real} A type defined by a real_type_definition is implicitly
derived from root_real, an anonymous predefined (specific) real type.
[Hence, all real types, whether floating point or fixed point, are in the
derivation class rooted at root_real.]

        3.a   Ramification:  It is not specified whether the derivation from
        root_real is direct or indirect, not that it really matters.  All we
        want is for all real types to be descendants of root_real.

4   [{universal_real [partial]} {real literals} Real literals are all of the
type universal_real, the universal type (see 3.4.1) for the class rooted at
root_real, allowing their use with the operations of any real type.
{universal_fixed [partial]} Certain multiplying operators have a result type
of universal_fixed (see 4.5.5), the universal type for the class of fixed
point types, allowing the result of the multiplication or division to be used
where any specific fixed point type is expected.]


                              Dynamic Semantics

5   {elaboration [real_type_definition]} The elaboration of a real_type_
definition consists of the elaboration of the floating_point_definition or
the fixed_point_definition.


                         Implementation Requirements

6   An implementation shall perform the run-time evaluation of a use of a
predefined operator of root_real with an accuracy at least as great as that
of any floating point type definable by a floating_point_definition.

        6.a   Ramification:  Static calculations using the operators of root_
        real are exact, as for all static calculations.  See 4.9.

        6.b   Implementation Note:  The Digits attribute of the type used to
        represent root_real at run time is at least as great as that of any
        other floating point type defined by a floating_point_definition, and
        its safe range includes that of any such floating point type with the
        same Digits attribute.  On some machines, there might be real types
        with less accuracy but a wider range, and hence run-time calculations
        with root_real might not be able to accommodate all values that can
        be represented at run time in such floating point or fixed point
        types.


                         Implementation Permissions

7   [For the execution of a predefined operation of a real type, the
implementation need not raise Constraint_Error if the result is outside the
base range of the type, so long as the correct result is produced, or the
Machine_Overflows attribute of the type is false (see G.2).]

8   {nonstandard real type}

        8.a   Implementation defined:  Any nonstandard real types and the
        operators defined for them.

An implementation may provide nonstandard real types, descendants of root_
real that are declared outside of the specification of package Standard,
which need not have all the standard characteristics of a type defined by a
real_type_definition.  For example, a nonstandard real type might have an
asymmetric or unsigned base range, or its predefined operations might wrap
around or ``saturate'' rather than overflow (modular or saturating
arithmetic), or it might not conform to the accuracy model (see G.2).  Any
type descended from a nonstandard real type is also nonstandard.  An
implementation may place arbitrary restrictions on the use of such types; it
is implementation defined whether operators that are predefined for ``any
real type'' are defined for a particular nonstandard real type.  [In any
case, such types are not permitted as explicit_generic_actual_parameters for
formal scalar types -- see 12.5.2.]


     NOTES
9    (32) As stated, real literals are of the anonymous predefined real type
     universal_real.  Other real types have no literals.  However, the
     overload resolution rules (see 8.6) allow expressions of the type
     universal_real whenever a real type is expected.


                         Wording Changes From Ada 83

        9.a   The syntax rule for real_type_definition is modified to use the
        new syntactic categories floating_point_definition and fixed_point_
        definition, instead of floating_point_constraint and fixed_point_
        constraint, because the semantics of a type definition are
        significantly different than the semantics of a constraint.

        9.b   All discussion of model numbers, safe ranges, and machine
        numbers is moved to 3.5.7, 3.5.8, and G.2.  Values of a fixed point
        type are now described as being multiples of the small of the fixed
        point type, and we have no need for model numbers, safe ranges, etc.
        for fixed point types.
3.5.7 Floating Point Types

1   {floating point type} For floating point types, the error bound is
specified as a relative precision by giving the required minimum number of
significant decimal digits.


                                   Syntax

2   floating_point_definition ::=
      digits static_expression [real_range_specification]

3   real_range_specification ::=
      range static_simple_expression .. static_simple_expression


                            Name Resolution Rules

4   {requested decimal precision (of a floating point type)} The requested
decimal precision, which is the minimum number of significant decimal digits
required for the floating point type, is specified by the value of the
expression given after the reserved word digits.  {expected type [requested
decimal precision]} This expression is expected to be of any integer type.

5   {expected type [real_range_specification bounds]} Each simple_expression
of a real_range_specification is expected to be of any real type[; the types
need not be the same].


                               Legality Rules

6   {Max_Base_Digits} The requested decimal precision shall be specified by a
static expression whose value is positive and no greater than System.Max_
Base_Digits.  Each simple_expression of a real_range_specification shall also
be static.  {Max_Digits} If the real_range_specification is omitted, the
requested decimal precision shall be no greater than System.Max_Digits.

        6.a   Reason:  We have added Max_Base_Digits to package System.  It
        corresponds to the requested decimal precision of root_real.
        System.Max_Digits corresponds to the maximum value for Digits that
        may be specified in the absence of a real_range_specification, for
        upward compatibility.  These might not be the same if root_real has a
        base range that does not include +/- 10.0**(4*Max_Base_Digits).

7   A floating_point_definition is illegal if the implementation does not
support a floating point type that satisfies the requested decimal precision
and range.

        7.a   Implementation defined:  What combinations of requested decimal
        precision and range are supported for floating point types.


                              Static Semantics

8   The set of values for a floating point type is the (infinite) set of
rational numbers.  {machine numbers (of a floating point type)} The machine
numbers of a floating point type are the values of the type that can be
represented exactly in every unconstrained variable of the type.  {base range
[of a floating point type]} The base range (see 3.5) of a floating point type
is symmetric around zero, except that it can include some extra negative
values in some implementations.

        8.a   Implementation Note:  For example, if a 2's complement
        representation is used for the mantissa rather than a sign-mantissa
        or 1's complement representation, then there is usually one extra
        negative machine number.

        8.b   To be honest:  If the Signed_Zeros attribute is True, then
        minus zero could in a sense be considered a value of the type.
        However, for most purposes, minus zero behaves the same as plus zero.
        {94-4448.a} {94-4889.e}

9   {base decimal precision (of a floating point type)} The base decimal
precision of a floating point type is the number of decimal digits of
precision representable in objects of the type.  {safe range (of a floating
point type)} The safe range of a floating point type is that part of its base
range for which the accuracy corresponding to the base decimal precision is
preserved by all predefined operations.

        9.a   Implementation Note:  In most cases, the safe range and base
        range are the same.  However, for some hardware, values near the
        boundaries of the base range might result in excessive inaccuracies
        or spurious overflows when used with certain predefined operations.
        For such hardware, the safe range would omit such values.

10   {base decimal precision [of a floating point type]} A floating_point_
definition defines a floating point type whose base decimal precision is no
less than the requested decimal precision.  {94-4935.a} {94-4913.f} {safe
range [of a floating point type]} {base range [of a floating point type]} If
a real_range_specification is given, the safe range of the floating point
type (and hence, also its base range) includes at least the values of the
simple expressions given in the real_range_specification.  If a real_range_
specification is not given, the safe (and base) range of the type includes at
least the values of the range -10.0**(4*D) .. +10.0**(4*D) where D is the
requested decimal precision.  [The safe range might include other values as
well.  The attributes Safe_First and Safe_Last give the actual bounds of the
safe range.]

11   A floating_point_definition also defines a first subtype of the type.
{constrained (subtype)} {unconstrained (subtype)} If a real_range_
specification is given, then the subtype is constrained to a range whose
bounds are given by a conversion of the values of the simple_expressions of
the real_range_specification to the type being defined.  {implicit subtype
conversion [bounds of a floating point type]} Otherwise, the subtype is
unconstrained.

12   {Float} There is a predefined, unconstrained, floating point subtype
named Float[, declared in the visible part of package Standard].


                              Dynamic Semantics

13   {elaboration [floating_point_definition]} [The elaboration of a
floating_point_definition creates the floating point type and its first
subtype.]


                         Implementation Requirements

14   {Float} In an implementation that supports floating point types with 6
or more digits of precision, the requested decimal precision for Float shall
be at least 6.

15   {Long_Float} If Long_Float is predefined for an implementation, then its
requested decimal precision shall be at least 11.


                         Implementation Permissions

16   {Short_Float} {Long_Float} An implementation is allowed to provide
additional predefined floating point types[, declared in the visible part of
Standard], whose (unconstrained) first subtypes have names of the form Short_
Float, Long_Float, Short_Short_Float, Long_Long_Float, etc.  Different
predefined floating point types are allowed to have the same base decimal
precision.  However, the precision of Float should be no greater than that of
Long_Float.  Similarly, the precision of Short_Float (if provided) should be
no greater than Float.  Corresponding recommendations apply to any other
predefined floating point types.  There need not be a named floating point
type corresponding to each distinct base decimal precision supported by an
implementation.

        16.a   Implementation defined:  The predefined floating point types
        declared in Standard.


                            Implementation Advice

17   {Long_Float} An implementation should support Long_Float in addition to
Float if the target machine supports 11 or more digits of precision.  No
other named floating point subtypes are recommended for package Standard.
Instead, appropriate named floating point subtypes should be provided in the
library package Interfaces (see B.2).

        17.a   Implementation Note:  To promote portability, implementations
        should explicitly declare the floating point (sub)types Float and
        Long_Float in Standard, and leave other predefined float types
        anonymous.  For implementations that already support Short_Float,
        etc., upward compatibility argues for keeping such declarations in
        Standard during the transition period, but perhaps generating a
        warning on use.  A separate package Interfaces in the predefined
        environment is available for pre-declaring types such as Float_32,
        IEEE_Float_64, etc.  See B.2.


     NOTES
18   (33) If a floating point subtype is unconstrained, then assignments to
     variables of the subtype involve only Overflow_Checks, never Range_
     Checks.


                                  Examples

19   Examples of floating point types and subtypes:

20  type Coefficient is digits 10 range -1.0 .. 1.0;

21  type Real is digits 8;
    type Mass is digits 7 range 0.0 .. 1.0E35;

22  subtype Probability is Real range 0.0 .. 1.0;   --   a subtype with a small\
er range


                         Inconsistencies With Ada 83

        22.a   {inconsistencies with Ada 83} No Range_Checks, only Overflow_
        Checks, are performed on variables (or parameters) of an
        unconstrained floating point subtype.  This is upward compatible for
        programs that do not raise Constraint_Error.  For those that do raise
        Constraint_Error, it is possible that the exception will be raised at
        a later point, or not at all, if extended range floating point
        registers are used to hold the value of the variable (or parameter).

        22.b   Reason:  This change was felt to be justified by the
        possibility of improved performance on machines with extended-range
        floating point registers.  An implementation need not take advantage
        of this relaxation in the range checking; it can hide completely the
        use of extended range registers if desired, presumably at some
        run-time expense.
                         Wording Changes From Ada 83

        22.c   The syntax rules for floating_point_constraint and floating_
        accuracy_definition are removed.  The syntax rules for floating_
        point_definition and real_range_specification are new.

        22.d   A syntax rule for digits_constraint is given in 3.5.9, ``Fixed
        Point Types''.  In J.3 we indicate that a digits_constraint may be
        applied to a floating point subtype_mark as well (to be compatible
        with Ada 83's floating_point_constraint).

        22.e   Discussion of model numbers is postponed to 3.5.8 and G.2.
        The concept of safe numbers has been replaced by the concept of the
        safe range of values.  The bounds of the safe range are given by
        T'Safe_First .. T'Safe_Last, rather than -T'Safe_Large ..  T'Safe_
        Large, since on some machines the safe range is not perfectly
        symmetric.  The concept of machine numbers is new, and is relevant to
        the definition of Succ and Pred for floating point numbers.



3.5.8 Operations of Floating Point Types

                              Static Semantics

1   The following attribute is defined for every floating point subtype S:

        1.a   Change:  Editorial change -- plural to singular in above
        phrase.

2   S'Digits
                S'Digits denotes the requested decimal precision for the
                subtype S. The value of this attribute is of the type
                universal_integer.  The requested decimal precision of the
                base subtype of a floating point type T is defined to be the
                largest value of d for which ceiling(d * log(10) /
                log(T'Machine_Radix)) + 1 <= T'Model_Mantissa.  {94-4935.a}
                {94-4913.f}


     NOTES
3    (34) {predefined operations [of a floating point type]} The predefined
     operations of a floating point type include the assignment operation,
     qualification, the membership tests, and explicit conversion to and from
     other numeric types.  They also include the relational operators and the
     following predefined arithmetic operators:  the binary and unary adding
     operators - and +, certain multiplying operators, the unary operator
     abs, and the exponentiation operator.  {94-4693.v}

4    (35) As for all types, objects of a floating point type have Size and
     Address attributes (see 13.3).  Other attributes of floating point types
     are defined in A.5.3.



3.5.9 Fixed Point Types

1   {fixed point type} {ordinary fixed point type} {decimal fixed point type}
A fixed point type is either an ordinary fixed point type, or a decimal fixed
point type.  {delta (of a fixed point type)} The error bound of a fixed point
type is specified as an absolute value, called the delta of the fixed point
type.


                                   Syntax

2   fixed_point_definition ::= ordinary_fixed_point_definition | decimal_fixed_\
point_definition

3   ordinary_fixed_point_definition ::=
       delta static_expression  real_range_specification

4   decimal_fixed_point_definition ::=
       delta static_expression digits static_expression [real_range_specificati\
on]

5   digits_constraint ::=
       digits static_expression [range_constraint]


                            Name Resolution Rules

6   {expected type [fixed point type delta]} For a type defined by a fixed_
point_definition, the delta of the type is specified by the value of the
expression given after the reserved word delta; this expression is expected
to be of any real type.  {expected type [decimal fixed point type digits]}
{digits (of a decimal fixed point subtype)} {decimal fixed point type} For a
type defined by a decimal_fixed_point_definition (a decimal fixed point
type), the number of significant decimal digits for its first subtype (the
digits of the first subtype) is specified by the expression given after the
reserved word digits; this expression is expected to be of any integer type.


                               Legality Rules

7   In a fixed_point_definition or digits_constraint, the expressions given
after the reserved words delta and digits shall be static; their values shall
be positive.

8   {small (of a fixed point type)} The set of values of a fixed point type
comprise the integral multiples of a number called the small of the type.
{ordinary fixed point type} For a type defined by an ordinary_fixed_point_
definition (an ordinary fixed point type), the small may be specified by an
attribute_definition_clause (see 13.3); if so specified, it shall be no
greater than the delta of the type.  If not specified, the small of an
ordinary fixed point type is an implementation-defined power of two less than
or equal to the delta.

        8.a   Implementation defined:  The small of an ordinary fixed point
        type.

9   For a decimal fixed point type, the small equals the delta; the delta
shall be a power of 10.  If a real_range_specification is given, both bounds
of the range shall be in the range -(10**digits-1)*delta ..
+(10**digits-1)*delta.

10   A fixed_point_definition is illegal if the implementation does not
support a fixed point type with the given small and specified range or
digits.

        10.a   Implementation defined:  What combinations of small, range,
        and digits are supported for fixed point types.

11   For a subtype_indication with a digits_constraint, the subtype_mark
shall denote a decimal fixed point subtype.

        11.a   To be honest:  Or, as an obsolescent feature, a floating point
        subtype is permitted -- see J.3.


                              Static Semantics

12   {base range [of a fixed point type]} The base range (see 3.5) of a fixed
point type is symmetric around zero, except possibly for an extra negative
value in some implementations.

13   {base range [of an ordinary fixed point type]} An ordinary_fixed_point_
definition defines an ordinary fixed point type whose base range includes at
least all multiples of small that are between the bounds specified in the
real_range_specification.  The base range of the type does not necessarily
include the specified bounds themselves.  {constrained (subtype)}
{unconstrained (subtype)} An ordinary_fixed_point_definition also defines a
constrained first subtype of the type, with each bound of its range given by
the closer to zero of:

   14  the value of the conversion to the fixed point type of the
       corresponding expression of the real_range_specification;
       {implicit subtype conversion [bounds of a fixed point type]}

   15  the corresponding bound of the base range.

16   {base range [of a decimal fixed point type]} A decimal_fixed_point_
definition defines a decimal fixed point type whose base range includes at
least the range -(10**digits-1)*delta .. +(10**digits-1)*delta.  {constrained
(subtype)} {unconstrained (subtype)} A decimal_fixed_point_definition also
defines a constrained first subtype of the type.  If a real_range_
specification is given, the bounds of the first subtype are given by a
conversion of the values of the expressions of the real_range_specification.
{implicit subtype conversion [bounds of a decimal fixed point type]}
Otherwise, the range of the first subtype is -(10**digits-1)*delta ..
+(10**digits-1)*delta.


                              Dynamic Semantics

17   {elaboration [fixed_point_definition]} The elaboration of a fixed_point_
definition creates the fixed point type and its first subtype.

18   For a digits_constraint on a decimal fixed point subtype with a given
delta, if it does not have a range_constraint, then it specifies an implicit
range -(10**D-1)*delta .. +(10**D-1)*delta, where D is the value of the
expression.  {compatibility (digits_constraint with a decimal fixed point
subtype)} A digits_constraint is compatible with a decimal fixed point
subtype if the value of the expression is no greater than the digits of the
subtype, and if it specifies (explicitly or implicitly) a range that is
compatible with the subtype.

        18.a   Discussion:  Except for the requirement that the digits
        specified be no greater than the digits of the subtype being
        constrained, a digits_constraint is essentially equivalent to a
        range_constraint.

        18.b   Consider the following example:

18.c        type D is delta 0.01 digits 7 range -0.00 .. 9999.99;

        18.d   The compatibility rule implies that the digits_constraint
        "digits 6" specifies an implicit range of "- 99.9999 .. 99.9999".
        Thus, "digits 6" is not compatible with the constraint of D, but
        "digits 6 range 0.00 .. 9999.99" is compatible.  {94-4502.a}

        18.e   A value of a scalar type belongs to a constrained subtype of
        the type if it belongs to the range of the subtype.  Attributes like
        Digits and Delta have no affect on this fundamental rule.  So the
        obsolescent forms of digits_constraints and delta_constraints that
        are called ``accuracy constraints'' in RM83 don't really represent
        constraints on the values of the subtype, but rather primarily affect
        compatibility of the ``constraint'' with the subtype being
        ``constrained.''  In this sense, they might better be called
        ``subtype assertions'' rather than ``constraints.''

        18.f   Note that the digits_constraint on a decimal fixed point
        subtype is a combination of an assertion about the digits of the
        subtype being further constrained, and a constraint on the range of
        the subtype being defined, either explicit or implicit.

19   {elaboration [digits_constraint]} The elaboration of a digits_constraint
consists of the elaboration of the range_constraint, if any.  {Range_Check
[partial]} {check, language-defined (Range_Check)} If a range_constraint is
given, a check is made that the bounds of the range are both in the range
-(10**D-1)*delta .. +(10**D-1)*delta, where D is the value of the (static)
expression given after the reserved word digits.  {Constraint_Error (raised
by failure of run-time check)} If this check fails, Constraint_Error is
raised.


                         Implementation Requirements

20   The implementation shall support at least 24 bits of precision
(including the sign bit) for fixed point types.

        20.a   Reason:  This is sufficient to represent Standard.Duration
        with a small no more than 50 milliseconds.


                         Implementation Permissions

21   Implementations are permitted to support only smalls that are a power of
two.  In particular, all decimal fixed point type declarations can be
disallowed.  Note however that conformance with the Information Systems Annex
requires support for decimal smalls, and decimal fixed point type
declarations with digits up to at least 18.

        21.a   Implementation Note:  The accuracy requirements for
        multiplication, division, and conversion (see G.2.1, ``Model of
        Floating Point Arithmetic'') are such that support for arbitrary
        smalls should be practical without undue implementation effort.
        Therefore, implementations should support fixed point types with
        arbitrary values for small (within reason).  One reasonable
        limitation would be to limit support to fixed point types that can be
        converted to the most precise floating point type without loss of
        precision (so that Fixed_IO is implementable in terms of Float_IO).


     NOTES
22   (36)  The base range of an ordinary fixed point type need not include
     the specified bounds themselves so that the range specification can be
     given in a natural way, such as:

23       type Fraction is delta 2.0**(-15) range -1.0 .. 1.0;

     24   With 2's complement hardware, such a type could have a signed
     16-bit representation, using 1 bit for the sign and 15 bits for
     fraction, resulting in a base range of -1.0 .. 1.0-2.0**(-15).


                                  Examples

25   Examples of fixed point types and subtypes:

26  type Volt is delta 0.125 range 0.0 .. 255.0;

27    --  A pure fraction which requires all the available
      --  space in a word can be declared as the type Fraction:
    type Fraction is delta System.Fine_Delta range -1.0 .. 1.0;
      --  Fraction'Last = 1.0 - System.Fine_Delta

28  type Money is delta 0.01 digits 15;  -- decimal fixed point
    subtype Salary is Money digits 10;
      -- Money'Last = 10.0**13 - 0.01, Salary'Last = 10.0**8 - 0.01


                         Inconsistencies With Ada 83

        28.a   {inconsistencies with Ada 83} In Ada 9X, S'Small always equals
        S'Base'Small, so if an implementation chooses a small for a fixed
        point type smaller than required by the delta, the value of S'Small
        in Ada 9X might not be the same as it was in Ada 83.

                            Extensions to Ada 83

        28.b   {extensions to Ada 83} Decimal fixed point types are new,
        though their capabilities are essentially similar to that available
        in Ada 83 with a fixed point type whose small equals its delta equals
        a power of 10.  However, in the Information Systems Annex, additional
        requirements are placed on the support of decimal fixed point types
        (e.g. a minimum of 18 digits of precision).

                         Wording Changes From Ada 83

        28.c   The syntax rules for fixed_point_constraint and fixed_
        accuracy_definition are removed.  The syntax rule for fixed_point_
        definition is new.  A syntax rule for delta_constraint is included in
        the Obsolescent features (to be compatible with Ada 83's fixed_point_
        constraint).



3.5.10 Operations of Fixed Point Types

                              Static Semantics

1   The following attributes are defined for every fixed point subtype S:

2   S'Small
                S'Small denotes the small of the type of S. The value of this
                attribute is of the type universal_real.  {specifiable [of
                Small for fixed point types]} {Small clause} Small may be
                specified for nonderived fixed point types via an attribute_
                definition_clause (see 13.3); the expression of such a clause
                shall be static.

3   S'Delta
                S'Delta denotes the delta of the fixed point subtype S. The
                value of this attribute is of the type universal_real.

3.a     Reason:  The delta is associated with the subtype as opposed to the
        type, because of the possibility of an (obsolescent) delta_
        constraint.

4   S'Fore
                S'Fore yields the minimum number of characters needed before
                the decimal point for the decimal representation of any value
                of the subtype S, assuming that the representation does not
                include an exponent, but includes a one-character prefix that
                is either a minus sign or a space.  (This minimum number does
                not include superfluous zeros or underlines, and is at least
                2.)  The value of this attribute is of the type universal_
                integer.

5   S'Aft
                S'Aft yields the number of decimal digits needed after the
                decimal point to accommodate the delta of the subtype S,
                unless the delta of the subtype S is greater than 0.1, in
                which case the attribute yields the value one.  [(S'Aft is
                the smallest positive integer N for which (10**N)*S'Delta is
                greater than or equal to one.)]  The value of this attribute
                is of the type universal_integer.

6   The following additional attributes are defined for every decimal fixed
point subtype S:

7   S'Digits
                S'Digits denotes the digits of the decimal fixed point
                subtype S, which corresponds to the number of decimal digits
                that are representable in objects of the subtype.  The value
                of this attribute is of the type universal_integer.  Its
                value is determined as follows:  {94-4768.k} {digits (of a
                decimal fixed point subtype)}

                    8  For a first subtype or a subtype defined by a
                       subtype_indication with a digits_constraint, the
                       digits is the value of the expression given after
                       the reserved word digits;

                    9  For a subtype defined by a subtype_indication
                       without a digits_constraint, the digits of the
                       subtype is the same as that of the subtype
                       denoted by the subtype_mark in the subtype_
                       indication.

 9.a    Implementation Note:  Although a decimal subtype can be both
        range-constrained and digits-constrained, the digits constraint
        is intended to control the Size attribute of the subtype.  For
        decimal types, Size can be important because input/output of
        decimal types is so common.

                   10  The digits of a base subtype is the largest
                       integer D such that the range -(10**D-1)*delta ..
                       +(10**D-1)*delta is included in the base range of
                       the type.

 10.a   Change:  Made 3.5.10(10);5.7 into a bullet under S'Digits, rather
        than separately listing it under S'Base'Digits, as per WG9
        resolution.

11  S'Scale
                S'Scale denotes the scale of the subtype S, defined as the
                value N such that S'Delta = 10.0**(-N).  {scale (of a decimal
                fixed point subtype)} [The scale indicates the position of
                the point relative to the rightmost significant digits of
                values of subtype S.]  The value of this attribute is of the
                type universal_integer.

11.a    Ramification:  S'Scale is negative if S'Delta is greater than one.
        By contrast, S'Aft is always positive.

12  S'Round
                S'Round denotes a function with the following specification:

13                  function S'Round(X : universal_real)
                      return S'Base

                14   The function returns the value obtained by rounding X
                (away from 0, if X is midway between two values of the type
                of S).
     NOTES
15   (37) All subtypes of a fixed point type will have the same value for the
     Delta attribute, in the absence of delta_constraints (see J.3).

16   (38) S'Scale is not always the same as S'Aft for a decimal subtype; for
     example, if S'Delta = 1.0 then S'Aft is 1 while S'Scale is 0.

17   (39) {predefined operations [of a fixed point type]} The predefined
     operations of a fixed point type include the assignment operation,
     qualification, the membership tests, and explicit conversion to and from
     other numeric types.  They also include the relational operators and the
     following predefined arithmetic operators:  the binary and unary adding
     operators - and +, multiplying operators, and the unary operator abs.

18   (40) As for all types, objects of a fixed point type have Size and
     Address attributes (see 13.3).  Other attributes of fixed point types
     are defined in A.5.4.



3.6 Array Types

1   {array} {array type} An array object is a composite object consisting of
components which all have the same subtype.  The name for a component of an
array uses one or more index values belonging to specified discrete types.
The value of an array object is a composite value consisting of the values of
the components.


                                   Syntax

2   array_type_definition ::=
       unconstrained_array_definition | constrained_array_definition

3   unconstrained_array_definition ::=
       array(index_subtype_definition {, index_subtype_definition}) of componen\
t_definition

4   index_subtype_definition ::= subtype_mark range <>

5   constrained_array_definition ::=
       array (discrete_subtype_definition {, discrete_subtype_definition}) of c\
omponent_definition

6   discrete_subtype_definition ::= discrete_subtype_indication | range

7   component_definition ::= [aliased] subtype_indication


                            Name Resolution Rules

8   {expected type [discrete_subtype_definition range]} For a discrete_
subtype_definition that is a range, the range shall resolve to be of some
specific discrete type[; which discrete type shall be determined without
using any context other than the bounds of the range itself (plus the
preference for root_integer -- see 8.6).]


                               Legality Rules

9   {index subtype} Each index_subtype_definition or discrete_subtype_
definition in an array_type_definition defines an index subtype; {index type}
its type (the index type) shall be discrete.

        9.a   Discussion:  {index (of an array)} An index is a discrete
        quantity used to select along a given dimension of an array.  A
        component is selected by specifying corresponding values for each of
        the indices.

10   {component subtype} The subtype defined by the subtype_indication of a
component_definition (the component subtype) shall be a definite subtype.

        10.a   Ramification:  This applies to all uses of component_
        definition, including in record_type_definitions and protected_
        definitions.

11   Within the definition of a nonlimited composite type (or a limited
composite type that later in its immediate scope becomes nonlimited -- see
7.3.1 and 7.5), if a component_definition contains the reserved word aliased
and the type of the component is discriminated, then the nominal subtype of
the component shall be constrained.

        11.a   Reason:  If we allowed the subtype to be unconstrained, then
        the discriminants might change because of an assignment to the
        containing (nonlimited) object, thus causing a potential violation of
        an access subtype constraint of an access value designating the
        aliased component.

        11.b   Note that the rule elsewhere defining all aliased
        discriminated objects to be constrained does not help -- that rule
        prevents assignments to the component itself from doing any harm, but
        not assignments to the containing object.  {94-4858.a}

        11.c   We allow this for components within limited types since
        assignment to the enclosing object is not a problem.  Furthermore, it
        is important to be able to use a default expression for a
        discriminant in arrays of limited components, since that is the only
        way to give the components different values for their discriminants.
        For example:

11.d        protected type Counter_Type(Initial_Value : Integer := 1) is
               procedure Get_Next(Next_Value : out Integer);
                 -- Returns the next value on each call, bumping Count
                 -- before returning.
            private
               Count : Integer := Initial_Value;
            end Counter_Type;
            protected body Counter_Type is ...

11.e        function Next_Id(Counter : access Counter_Type) return Integer is
                Result : Integer;
            begin
                Counter.Get_Next(Result);
                return Result;
            end Next_Id;

11.f        C : aliased Counter_Type;
            task type T(Who_Am_I : Integer := Next_Id(C'Access));
            task body T is ...

11.g        Task_Array : array(1..100) of aliased T;
              -- Array of task elements, each with its own unique ID.
              -- We specify "aliased" so we can use Task_Array(I)'Access.
              -- This is safe because Task_Array is of a limited type,
              -- so there is no way an assignment to it could change
              -- the discriminants of one of its components.

        11.h   Ramification:  Note that this rule applies to array components
        and record components, but not to protected type components (since
        they are always limited).


                              Static Semantics

12   {dimensionality (of an array)} {one-dimensional array} {multi-
dimensional array} An array is characterized by the number of indices (the
dimensionality of the array), the type and position of each index, the lower
and upper bounds for each index, and the subtype of the components.  The
order of the indices is significant.

13   A one-dimensional array has a distinct component for each possible index
value.  A multidimensional array has a distinct component for each possible
sequence of index values that can be formed by selecting one value for each
index position (in the given order).  The possible values for a given index
are all the values between the lower and upper bounds, inclusive; {index
range} this range of values is called the index range.  {bounds (of an
array)} The bounds of an array are the bounds of its index ranges.  {length
(of a dimension of an array)} The length of a dimension of an array is the
number of values of the index range of the dimension (zero for a null range).
{length (of a one-dimensional array)} The length of a one-dimensional array
is the length of its only dimension.

14   An array_type_definition defines an array type and its first subtype.
For each object of this array type, the number of indices, the type and
position of each index, and the subtype of the components are as in the type
definition[; the values of the lower and upper bounds for each index belong
to the corresponding index subtype of its type, except for null arrays (see
3.6.1)].

15   {constrained (subtype)} {unconstrained (subtype)} An unconstrained_
array_definition defines an array type with an unconstrained first subtype.
Each index_subtype_definition defines the corresponding index subtype to be
the subtype denoted by the subtype_mark.[{box [compound delimiter]} The
compound delimiter <> (called a box) of an index_subtype_definition stands
for an undefined range (different objects of the type need not have the same
bounds).]

16   {constrained (subtype)} {unconstrained (subtype)} A constrained_array_
definition defines an array type with a constrained first subtype.  Each
discrete_subtype_definition defines the corresponding index subtype, as well
as the corresponding index range for the constrained first subtype.
{constraint [of a first array subtype]} The constraint of the first subtype
consists of the bounds of the index ranges.

        16.a   Discussion:  Although there is no namable unconstrained array
        subtype in this case, the predefined slicing and concatenation
        operations can operate on and yield values that do not necessarily
        belong to the first array subtype.  This is also true for Ada 83.

17   The discrete subtype defined by a discrete_subtype_definition is either
that defined by the subtype_indication, or a subtype determined by the range
as follows:

   18  If the type of the range resolves to root_integer, then the
       discrete_subtype_definition defines a subtype of the predefined
       type Integer with bounds given by a conversion to Integer of the
       bounds of the range; {implicit subtype conversion [bounds of a
       range]}

 18.a   Reason:  This ensures that indexing over the discrete subtype
        can be performed with regular Integers, rather than only
        universal_integers.

 18.b   Discussion:  We considered doing this by simply creating a
        ``preference'' for Integer when resolving the range.
        {Beaujolais effect [partial]} However, this can introduce
        Beaujolais effects when the simple_expressions involve calls on
        functions visible due to use clauses.

   19  Otherwise, the discrete_subtype_definition defines a subtype of
       the type of the range, with the bounds given by the range.

20   {nominal subtype [of a component]} The component_definition of an array_
type_definition defines the nominal subtype of the components.  If the
reserved word aliased appears in the component_definition, then each
component of the array is aliased (see 3.10).

        20.a   Ramification:  In this case, the nominal subtype cannot be an
        unconstrained discriminated subtype.  See 3.8.


                              Dynamic Semantics

21   {elaboration [array_type_definition]} The elaboration of an array_type_
definition creates the array type and its first subtype, and consists of the
elaboration of any discrete_subtype_definitions and the component_definition.

22   {elaboration [discrete_subtype_definition]} The elaboration of a
discrete_subtype_definition creates the discrete subtype, and consists of the
elaboration of the subtype_indication or the evaluation of the range.
{elaboration [component_definition]} The elaboration of a component_
definition in an array_type_definition consists of the elaboration of the
subtype_indication.  The elaboration of any discrete_subtype_definitions and
the elaboration of the component_definition are performed in an arbitrary
order.


     NOTES
23   (41) All components of an array have the same subtype.  In particular,
     for an array of components that are one-dimensional arrays, this means
     that all components have the same bounds and hence the same length.

24   (42) Each elaboration of an array_type_definition creates a distinct
     array type.  A consequence of this is that each object whose object_
     declaration contains an array_type_definition is of its own unique type.


                                  Examples

25   Examples of type declarations with unconstrained array definitions:

26  type Vector     is array(Integer  range <>) of Real;
    type Matrix     is array(Integer  range <>, Integer range <>) of Real;
    type Bit_Vector is array(Integer  range <>) of Boolean;
    type Roman      is array(Positive range <>) of Roman_Digit; -- see 3.5.2

27   Examples of type declarations with constrained array definitions:

28  type Table    is array(1 .. 10) of Integer;
    type Schedule is array(Day) of Boolean;
    type Line     is array(1 .. Max_Line_Size) of Character;

29   Examples of object declarations with array type definitions:

30  Grid : array(1 .. 80, 1 .. 100) of Boolean;
    Mix  : array(Color range Red .. Green) of Boolean;
    Page : array(Positive range <>) of Line :=  --  an array of arrays
      (1 | 50  => Line'(1 | Line'Last => '+', others => '-'),  -- see 4.3.3
       2 .. 49 => Line'(1 | Line'Last => '|', others => ' '));
        -- Page is constrained by its initial value to (1..50)


                            Extensions to Ada 83

        30.a   {extensions to Ada 83} The syntax rule for component_
        definition is modified to allow the reserved word aliased.

        30.b   The syntax rules for unconstrained_array_definition and
        constrained_array_definition are modified to use component_definition
        (instead of component_subtype_indication).  The effect of this change
        is to allow the reserved word aliased before the component subtype_
        indication.

        30.c   A range in a discrete_subtype_definition may use arbitrary
        universal expressions for each bound (e.g. -1 .. 3+5), rather than
        strictly "implicitly convertible" operands.  The subtype defined will
        still be a subtype of Integer.

                         Wording Changes From Ada 83

        30.d   We introduce a new syntactic category, discrete_subtype_
        definition, as distinct from discrete_range.  These two constructs
        have the same syntax, but their semantics are quite different (one
        defines a subtype, with a preference for Integer subtypes, while the
        other just selects a subrange of an existing subtype).  We use this
        new syntactic category in for loops and entry families.

        30.e   The syntax for index_constraint and discrete_range have been
        moved to their own subclause, since they are no longer used here.

        30.f   The syntax rule for component_definition (formerly component_
        subtype_definition) is moved here from RM83-3.7.



3.6.1 Index Constraints and Discrete Ranges

1   An index_constraint determines the range of possible values for every
index of an array subtype, and thereby the corresponding array bounds.


                                   Syntax

2   index_constraint ::=  (discrete_range {, discrete_range})

3   discrete_range ::= discrete_subtype_indication | range


                            Name Resolution Rules

4   {type of a discrete_range} The type of a discrete_range is the type of
the subtype defined by the subtype_indication, or the type of the range.
{expected type [index_constraint discrete_range]} For an index_constraint,
each discrete_range shall resolve to be of the type of the corresponding
index.

        4.a   Discussion:  In Ada 9X, index_constraints only appear in a
        subtype_indication; they no longer appear in constrained_array_
        definitions.


                               Legality Rules

5   An index_constraint shall appear only in a subtype_indication whose
subtype_mark denotes either an unconstrained array subtype, or an
unconstrained access subtype whose designated subtype is an unconstrained
array subtype; in either case, the index_constraint shall provide a discrete_
range for each index of the array type.


                              Static Semantics

6   {bounds (of a discrete_range)} A discrete_range defines a range whose
bounds are given by the range, or by the range of the subtype defined by the
subtype_indication.


                              Dynamic Semantics

7   {compatibility [index constraint with a subtype]} An index_constraint is
compatible with an unconstrained array subtype if and only if the index range
defined by each discrete_range is compatible (see 3.5) with the corresponding
index subtype.  {null array} If any of the discrete_ranges defines a null
range, any array thus constrained is a null array, having no components.
{satisfies [an index constraint]} An array value satisfies an index_
constraint if at each index position the array value and the index_constraint
have the same index bounds.

        7.a   Ramification:  There is no need to define compatibility with a
        constrained array subtype, because one is not allowed to constrain it
        again.

8   {elaboration [index_constraint]} The elaboration of an index_constraint
consists of the evaluation of the discrete_range(s), in an arbitrary order.
{evaluation [discrete_range]} The evaluation of a discrete_range consists of
the elaboration of the subtype_indication or the evaluation of the range.


     NOTES
9    (43) The elaboration of a subtype_indication consisting of a subtype_
     mark followed by an index_constraint checks the compatibility of the
     index_constraint with the subtype_mark (see 3.2.2).

10   (44) Even if an array value does not satisfy the index constraint of an
     array subtype, Constraint_Error is not raised on conversion to the array
     subtype, so long as the length of each dimension of the array value and
     the array subtype match.  See 4.6.


                                  Examples

11   Examples of array declarations including an index constraint:

12  Board     : Matrix(1 .. 8,  1 .. 8);  --  see 3.6
    Rectangle : Matrix(1 .. 20, 1 .. 30);
    Inverse   : Matrix(1 .. N,  1 .. N);  --  N need not be static

13  Filter    : Bit_Vector(0 .. 31);

14   Example of array declaration with a constrained array subtype:

15  My_Schedule : Schedule;  --  all arrays of type Schedule have the same boun\
ds

16   Example of record type with a component that is an array:

17  type Var_Line(Length : Natural) is
       record
          Image : String(1 .. Length);
       end record;

18  Null_Line : Var_Line(0);  --  Null_Line.Image is a null array


                            Extensions to Ada 83

        18.a   {extensions to Ada 83} We allow the declaration of a variable
        with a nominally unconstrained array subtype, so long as it has an
        initialization expression to determine its bounds.
                         Wording Changes From Ada 83

        18.b   We have moved the syntax for index_constraint and discrete_
        range here since they are no longer used in constrained_array_
        definitions.  We therefore also no longer have to describe the
        (special) semantics of index_constraints and discrete_ranges that
        appear in constrained_array_definitions.

        18.c   The rules given in RM83-3.6.1(5,7-10), which define the bounds
        of an array object, are redundant with rules given elsewhere, and so
        are not repeated here.  RM83-3.6.1(6), which requires that the
        (nominal) subtype of an array variable be constrained, no longer
        applies, so long as the variable is explicitly initialized.



3.6.2 Operations of Array Types

                               Legality Rules

1   [The argument N used in the attribute_designators for the N-th dimension
of an array shall be a static expression of some integer type.]  The value of
N shall be positive (nonzero) and no greater than the dimensionality of the
array.


                              Static Semantics

2   The following attributes are defined for a prefix A that is of an array
type [(after any implicit dereference)], or denotes a constrained array
subtype:

        2.a   Ramification:  These attributes are not defined if A is a
        subtype-mark for an access-to-array subtype.  They are defined (by
        implicit dereference) for access-to-array values.

3   A'First
                A'First denotes the lower bound of the first index range; its
                type is the corresponding index type.

4   A'First(N)
                A'First(N) denotes the lower bound of the N-th index range;
                its type is the corresponding index type.

5   A'Last
                A'Last denotes the upper bound of the first index range; its
                type is the corresponding index type.

6   A'Last(N)
                A'Last(N) denotes the upper bound of the N-th index range;
                its type is the corresponding index type.

7   A'Range
                A'Range is equivalent to the range A'First .. A'Last, except
                that the prefix A is only evaluated once.

8   A'Range(N)
                A'Range(N) is equivalent to the range A'First(N) ..
                A'Last(N), except that the prefix A is only evaluated once.

9   A'Length
                A'Length denotes the number of values of the first index
                range (zero for a null range); its type is universal_integer.

10  A'Length(N)
                A'Length(N) denotes the number of values of the N-th index
                range (zero for a null range); its type is universal_integer.


                            Implementation Advice

11   An implementation should normally represent multidimensional arrays in
row-major order, consistent with the notation used for multidimensional array
aggregates (see 4.3.3).  However, if a pragma Convention(Fortran, ...)
applies to a multidimensional array type, then column-major order should be
used instead (see B.5, ``Interfacing with Fortran'').


     NOTES
12   (45) The attribute_references A'First and A'First(1) denote the same
     value.  A similar relation exists for the attribute_references A'Last,
     A'Range, and A'Length.  The following relation is satisfied (except for
     a null array) by the above attributes if the index type is an integer
     type:

13       A'Length(N) = A'Last(N) - A'First(N) + 1

14   (46) An array type is limited if its component type is limited (see
     7.5).

15   (47) {predefined operations [of an array type]} The predefined
     operations of an array type include the membership tests, qualification,
     and explicit conversion.  If the array type is not limited, they also
     include assignment and the predefined equality operators.  For a
     one-dimensional array type, they include the predefined concatenation
     operators (if nonlimited) and, if the component type is discrete, the
     predefined relational operators; if the component type is boolean, the
     predefined logical operators are also included.

16   (48) A component of an array can be named with an indexed_component.  A
     value of an array type can be specified with an array_aggregate, unless
     the array type is limited.  For a one-dimensional array type, a slice of
     the array can be named; also, string literals are defined if the
     component type is a character type.


                                  Examples

17   Examples (using arrays declared in the examples of subclause 3.6.1):

18  --  Filter'First       =    0   Filter'Last        =  31   Filter'Length  =\
  32
    --  Rectangle'Last(1)  =   20   Rectangle'Last(2)  =  30



3.6.3 String Types

                              Static Semantics

1   {string type} A one-dimensional array type whose component type is a
character type is called a string type.

2   [There are two predefined string types, String and Wide_String, each
indexed by values of the predefined subtype Positive; these are declared in
the visible part of package Standard:

3   subtype Positive is Integer range 1 .. Integer'Last;

4   type String is array(Positive range <>) of Character;
    type Wide_String is array(Positive range <>) of Wide_Character;

]


     NOTES
5    (49) String literals (see 2.6 and 4.2) are defined for all string types.
     The concatenation operator & is predefined for string types, as for all
     nonlimited one-dimensional array types.  The ordering operators <, <=,
     >, and >= are predefined for string types, as for all one-dimensional
     discrete array types; these ordering operators correspond to
     lexicographic order (see 4.5.2).


                                  Examples

6   Examples of string objects:

7   Stars      : String(1 .. 120) := (1 .. 120 => '*' );
    Question   : constant String  := "How many characters?";
                                                   --  Question'First = 1, Ques\
tion'Last = 20
                                                   --  Question'Length = 20 (th\
e number of characters)

8   Ask_Twice  : String  := Question & Question;   --  constrained to (1..40)
    Ninety_Six : constant Roman   := "XCVI";      --  see 3.5.2 and 3.6


                         Inconsistencies With Ada 83

        8.a   {inconsistencies with Ada 83} The declaration of Wide_String in
        Standard hides a use-visible declaration with the same defining_
        identifier.  In rare cases, this might result in an inconsistency
        between Ada 83 and Ada 9X.

                        Incompatibilities With Ada 83

        8.b   {incompatibilities with Ada 83} Because both String and Wide_
        String are always directly visible, an expression like

8.c         "a" < "bc"

        8.d   is now ambiguous, whereas in Ada 83 both string literals could
        be resolved to type String.

                            Extensions to Ada 83

        8.e   {extensions to Ada 83} The type Wide_String is new (though it
        was approved by ARG for Ada 83 compilers as well).

                         Wording Changes From Ada 83

        8.f   We define the term string type as a natural analogy to the term
        character type.



3.7 Discriminants

1   [{discriminant} {type parameter: see discriminant} {parameter: see also
discriminant} A composite type (other than an array type) can have
discriminants, which parameterize the type.  A known_discriminant_part
specifies the discriminants of a composite type.  A discriminant of an object
is a component of the object, and is either of a discrete type or an access
type.  An unknown_discriminant_part in the declaration of a partial view of a
type specifies that the discriminants of the type are unknown for the given
view; all subtypes of such a partial view are indefinite subtypes.]

        1.a   Glossary entry:  {Discriminant} A discriminant is a parameter
        of a composite type.  It can control, for example, the bounds of a
        component of the type if that type is an array type.  A discriminant
        of a task type can be used to pass data to a task of the type upon
        creation.

        1.b   Discussion:  {unknown discriminants [partial]} {discriminants
        [unknown]} A type, and all of its subtypes, have unknown
        discriminants when the number or names of the discriminants, if any,
        are unknown at the point of the type declaration.  A discriminant_
        part of (<>) is used to indicate unknown discriminants.


                                   Syntax

2   discriminant_part ::= unknown_discriminant_part | known_discriminant_part

3   unknown_discriminant_part ::= (<>)

4   known_discriminant_part ::=
       (discriminant_specification {; discriminant_specification})

5   discriminant_specification ::=
       defining_identifier_list : subtype_mark [:= default_expression]
     | defining_identifier_list : access_definition [:= default_expression]

6   default_expression ::= expression


                            Name Resolution Rules

7   {expected type [discriminant default_expression]} The expected type for
the default_expression of a discriminant_specification is that of the
corresponding discriminant.


                               Legality Rules

8   A known_discriminant_part is only permitted in a declaration for a
composite type that is not an array type [(this includes generic formal
types)]; {discriminated type} a type declared with a known_discriminant_part
is called a discriminated type, as is a type that inherits (known)
discriminants.

        8.a   Implementation Note:  Discriminants on array types were
        considered, but were omitted to ease (existing) implementations.

        8.b   Discussion:  Note that the above definition for ``discriminated
        type'' does not include types declared with an unknown_discriminant_
        part.  This seems consistent with Ada 83, where such types (in a
        generic formal part) would not be considered discriminated types.
        Furthermore, the full type for a type with unknown discriminants need
        not even be composite, much less have any discriminants.

9   The subtype of a discriminant may be defined by a subtype_mark, in which
case the subtype_mark shall denote a discrete or access subtype, or it may be
defined by an access_definition [(in which case the subtype_mark of the
access_definition may denote any kind of subtype)].  {access discriminant} A
discriminant that is defined by an access_definition is called an access
discriminant and is of an anonymous general access-to-variable type whose
designated subtype is denoted by the subtype_mark of the access_definition.

        9.a   Reason:  In an earlier version of Ada 9X, we allowed access
        discriminants on nonlimited types, but this created unpleasant
        complexities.  It turned out to be simpler and more uniform to allow
        discriminants of a named access type on any discriminated type, and
        keep access discriminants just for limited types.

        9.b   Note that discriminants of a named access type are not
        considered ``access discriminants.''  Similarly, ``access parameter''
        only refers to a formal parameter defined by an access_definition.

10   A discriminant_specification for an access discriminant shall appear
only in the declaration for a task or protected type, or for a type with the
reserved word limited in its [(full)] definition or in that of one of its
ancestors.  In addition to the places where Legality Rules normally apply
(see 12.3), this rule applies also in the private part of an instance of a
generic unit.

        10.a   Discussion:  This rule implies that a type can have an access
        discriminant if the type is limited, but not if the only reason it's
        limited is because of a limited component.  Compare with the
        definition of limited type in 7.5.

        10.b   Ramification:  It is a consequence of this rule that only a
        return-by-reference type can have an access discriminant (see 6.5).
        This is important to avoid dangling references to local variables.

        10.c   Reason:  We also considered the following rules:

         10.d  If a type has an access discriminant, this automatically
               makes it limited, just like having a limited component
               automatically makes a type limited.  This was rejected
               because it decreases program readability, and because it
               seemed error prone (two bugs in a previous version of the
               RM9X were attributable to this rule).

         10.e  A type with an access discriminant shall be limited.
               This is equivalent to the rule we actually chose, except
               that it allows a type to have an access discriminant if
               it is limited just because of a limited component.  For
               example, any record containing a task would be allowed to
               have an access discriminant, whereas the actual rule
               requires ``limited record''.  This rule was also rejected
               due to readability concerns, and because would interact
               badly with the rules for limited types that ``become
               nonlimited''.

11   Default_expressions shall be provided either for all or for none of the
discriminants of a known_discriminant_part.  No default_expressions are
permitted in a known_discriminant_part in a declaration of a tagged type [or
a generic formal type].

        11.a   Reason:  The all-or-none rule is related to the rule that a
        discriminant constraint shall specify values for all discriminants.
        One could imagine a different rule that allowed a constraint to
        specify only some of the discriminants, with the others provided by
        default.  Having defaults for discriminants has a special
        significance -- it allows objects of the type to be unconstrained,
        with the discriminants alterable as part of assigning to the object.

        11.b   Defaults for discriminants of tagged types are disallowed so
        that every object of a tagged type is constrained, either by an
        explicit constraint, or by its initial discriminant values.
        {94-4858.a} This substantially simplifies the semantic rules and the
        implementation of inherited dispatching operations.  For generic
        formal types, the restriction simplifies the type matching rules.  If
        one simply wants a "default" value for the discriminants, a
        constrained subtype can be declared for future use.

12   For a type defined by a derived_type_definition, if a known_
discriminant_part is provided in its declaration, then:

   13  The parent subtype shall be constrained;

   14  If the parent type is not a tagged type, then each discriminant
       of the derived type shall be used in the constraint defining the
       parent subtype;

 14.a   Implementation Note:  This ensures that the new discriminant can
        share storage with an existing discriminant.

   15  If a discriminant is used in the constraint defining the parent
       subtype, the subtype of the discriminant shall be statically
       compatible (see 4.9.1) with the subtype of the corresponding
       parent discriminant.

 15.a   Reason:  This ensures that on conversion (or extension via an
        extension aggregate) to a distantly related type, if the
        discriminants satisfy the target type's requirements they
        satisfy all the intermediate types' requirements as well.

 15.b   Ramification:  There is no requirement that the new discriminant
        have the same (or any) default_expression as the parent's
        discriminant.

16   The type of the default_expression, if any, for an access discriminant
shall be convertible to the anonymous access type of the discriminant (see
4.6).  {convertible [required]}

        16.a   Ramification:  This requires convertibility of the designated
        subtypes.


                              Static Semantics

17   A discriminant_specification declares a discriminant; the subtype_mark
denotes its subtype unless it is an access discriminant, in which case the
discriminant's subtype is the anonymous access-to-variable subtype defined by
the access_definition.

18   [For a type defined by a derived_type_definition, each discriminant of
the parent type is either inherited, constrained to equal some new
discriminant of the derived type, or constrained to the value of an
expression.]  {corresponding discriminants} When inherited or constrained to
equal some new discriminant, the parent discriminant and the discriminant of
the derived type are said to correspond.  Two discriminants also correspond
if there is some common discriminant to which they both correspond.  A
discriminant corresponds to itself as well.  {specified discriminant} If a
discriminant of a parent type is constrained to a specific value by a
derived_type_definition, then that discriminant is said to be specified by
that derived_type_definition.

        18.a   Ramification:  The correspondence relationship is transitive,
        symmetric, and reflexive.  That is, if A corresponds to B, and B
        corresponds to C, then A, B, and C each corresponds to A, B, and C in
        all combinations.

19   {depend on a discriminant (for a constraint or component_definition)} A
constraint that appears within the definition of a discriminated type depends
on a discriminant of the type if it names the discriminant as a bound or
discriminant value.  A component_definition depends on a discriminant if its
constraint depends on the discriminant, or on a discriminant that corresponds
to it.

        19.a   Ramification:  A constraint in a task_body is not considered
        to depend on a discriminant of the task type, even if it names it.
        It is only the constraints in the type definition itself that are
        considered dependents.  Similarly for protected types.

20   {depend on a discriminant (for a component)} A component depends on a
discriminant if:
   21  Its component_definition depends on the discriminant; or

 21.a   Ramification:  A component does not depend on a discriminant
        just because its default_expression refers to the discriminant.

   22  It is declared in a variant_part that is governed by the
       discriminant; or

   23  It is a component inherited as part of a derived_type_definition,
       and the constraint of the parent_subtype_indication depends on
       the discriminant; or

 23.a   Reason:  When the parent subtype depends on a discriminant, the
        parent part of the derived type is treated like a
        discriminant-dependent component.

 23.b   Ramification:  Because of this rule, we don't really need to
        worry about ``corresponding'' discriminants, since all the
        inherited components will be discriminant-dependent if there is
        a new known_discriminant_part whose discriminants are used to
        constrain the old discriminants.

   24  It is a subcomponent of a component that depends on the
       discriminant.

        24.a   Reason:  The concept of discriminant-dependent (sub)components
        is primarily used in various rules that disallow renaming or 'Access,
        or specify that certain discriminant-changing assignments are
        erroneous.  The goal is to allow implementations to move around or
        change the size of discriminant-dependent subcomponents upon a
        discriminant-changing assignment to an enclosing object.  The above
        definition specifies that all subcomponents of a discriminant-
        dependent component or parent part are themselves discriminant-
        dependent, even though their presence or size does not in fact depend
        on a discriminant.  This is because it is likely that they will move
        in a discriminant-changing assignment if they are a component of one
        of several discriminant-dependent parts of the same record.

25   Each value of a discriminated type includes a value for each component
of the type that does not depend on a discriminant[; this includes the
discriminants themselves].  The values of discriminants determine which other
component values are present in the value of the discriminated type.

        25.a   To be honest:  Which values are present might depend on
        discriminants of some ancestor type that are constrained in an
        intervening derived_type_definition.  That's why we say "values of
        discriminants" instead of "values of the discriminants" -- a subtle
        point.

26   {known discriminants} {discriminants (known)} {constrained (subtype)}
{unconstrained (subtype)} A type declared with a known_discriminant_part is
said to have known discriminants; its first subtype is unconstrained.
{unknown discriminants} {discriminants (unknown)} A type declared with an
unknown_discriminant_part is said to have unknown discriminants.  A type
declared without a discriminant_part has no discriminants, unless it is a
derived type; if derived, such a type has the same sort of discriminants
(known, unknown, or none) as its parent (or ancestor) type.  A tagged
class-wide type also has unknown discriminants.  {class-wide type}
{indefinite subtype} [Any subtype of a type with unknown discriminants is an
unconstrained and indefinite subtype (see 3.2 and 3.3).]  {94-4610.a}

        26.a   Discussion:  An unknown_discriminant_part ``(<>)'' is only
        permitted in the declaration of a (generic or nongeneric) private
        type, private extension, or formal derived type.  Hence, only such
        types, descendants thereof, and class-wide types can have unknown
        discriminants.  An unknown_discriminant_part is used to indicate that
        the corresponding actual or full type might have discriminants
        without defaults, or be an unconstrained array subtype.  Tagged
        class-wide types are also considered to have unknown discriminants
        because discriminants can be added by type extensions, so the total
        number of discriminants of any given value of a tagged class-wide
        type is not known at compile time.

        26.b   A subtype with unknown discriminants is indefinite, and hence
        an object of such a subtype needs explicit initialization.  If the
        subtype is limited, no (stand-alone) objects can be declared since
        initialization is not permitted (though formal parameters are
        permitted, and objects of the actual/full type will generally be
        declarable).  A limited private type with unknown discriminants is
        ``extremely'' limited; such a type is useful for keeping complete
        control over object creation within the package declaring the type.

        26.c   A partial view of a type might have unknown discriminants,
        while the full view of the same type might have known, unknown, or no
        discriminants,


                              Dynamic Semantics

27   An access_definition is elaborated when the value of a corresponding
access discriminant is defined, either by evaluation of its default_
expression or by elaboration of a discriminant_constraint.  [The elaboration
of an access_definition creates the anonymous access type.  When the
expression defining the access discriminant is evaluated, it is converted to
this anonymous access type (see 4.6).]  {implicit subtype conversion [access
discriminant]}

        27.a   Ramification:  This conversion raises Constraint_Error if the
        initial value is null, or, for an object created by an allocator of
        an access type T, if the initial value is an access parameter that
        designates a view whose accessibility level is deeper than that of
        T. {94-4715.a}


     NOTES
28   (50) If a discriminated type has default_expressions for its
     discriminants, then unconstrained variables of the type are permitted,
     and the values of the discriminants can be changed by an assignment to
     such a variable.  If defaults are not provided for the discriminants,
     then all variables of the type are constrained, either by explicit
     constraint or by their initial value; the values of the discriminants of
     such a variable cannot be changed after initialization.

   28.a   Discussion:  This connection between discriminant defaults and
        unconstrained variables can be a source of confusion.  For Ada 9X, we
        considered various ways to break the connection between defaults and
        unconstrainedness, but ultimately gave up for lack of a sufficiently
        simple and intuitive alternative.

   28.b   {mutable} An unconstrained discriminated subtype with defaults is
        called a mutable subtype, and a variable of such a subtype is called
        a mutable variable, because the discriminants of such a variable can
        change.  There are no mutable arrays (that is, the bounds of an array
        object can never change), because there is no way in the language to
        define default values for the bounds.  Similarly, there are no
        mutable class-wide subtypes, because there is no way to define the
        default tag, and defaults for discriminants are not allowed in the
        tagged case.  Mutable tags would also require a way for the maximum
        possible size of such a class-wide subtype to be known.  (In some
        implementations, all mutable variables are allocated with the maximum
        possible size.  This approach is appropriate for real-time
        applications where implicit use of the heap is inappropriate.)
        {94-4799.a} {94-4801.a} {94-4806.a} {94-4874.a} {94-4882.a}

29   (51) The default_expression for a discriminant of a type is evaluated
     when an object of an unconstrained subtype of the type is created.

30   (52) Assignment to a discriminant of an object (after its
     initialization) is not allowed, since the name of a discriminant is a
     constant; neither assignment_statements nor assignments inherent in
     passing as an in out or out parameter are allowed.  Note however that
     the value of a discriminant can be changed by assigning to the enclosing
     object, presuming it is an unconstrained variable.

   30.a   Discussion:  An unknown_discriminant_part is permitted only in the
        declaration of a private type (including generic formal private),
        private extension, or generic formal derived type.  These are the
        things that will have a corresponding completion or generic actual,
        which will either define the discriminants, or say there are none.
        The (<>) indicates that the actual/full subtype might be an
        indefinite subtype.  An unknown_discriminant_part is not permitted in
        a normal untagged derived type declaration, because there is no
        separate full type declaration for such a type.  Note that (<>)
        allows unconstrained array bounds; those are somewhat like
        undefaulted discriminants.

   30.b   For a derived type, either the discriminants are inherited as is,
        or completely respecified in a new discriminant_part.  In this latter
        case, each discriminant of the parent type shall be constrained,
        either to a specific value, or to equal one of the new discriminants.
        Constraining a parent type's discriminant to equal one of the new
        discriminants is like a renaming of the discriminant, except that the
        subtype of the new discriminant can be more restrictive than that of
        the parent's one.  In any case, the new discriminant can share
        storage with the parent's discriminant.

31   (53) A discriminant that is of a named access type is not called an
     access discriminant; that term is used only for discriminants defined by
     an access_definition.


                                  Examples

32   Examples of discriminated types:

33  type Buffer(Size : Buffer_Size := 100)  is        -- see 3.5.4
       record
          Pos   : Buffer_Size := 0;
          Value : String(1 .. Size);
       end record;

34  type Matrix_Rec(Rows, Columns : Integer) is
       record
          Mat : Matrix(1 .. Rows, 1 .. Columns);       -- see 3.6
       end record;

35  type Square(Side : Integer) is new Matrix_Rec(Rows => Side, Columns => Side\
);

36  type Double_Square(Number : Integer) is
       record
          Left  : Square(Number);
          Right : Square(Number);
       end record;

37  type Item(Number : Positive) is
       record
          Content : Integer;
          --  no component depends on the discriminant
       end record;
                            Extensions to Ada 83

        37.a   {extensions to Ada 83} The syntax for a discriminant_
        specification is modified to allow an access discriminant, with a
        type specified by an access_definition (see 3.10).

        37.b   Discriminants are allowed on all composite types other than
        array types.

        37.c   Discriminants may be of an access type.

                         Wording Changes From Ada 83

        37.d   Discriminant_parts are not elaborated, though an access_
        definition is elaborated when the discriminant is initialized.



3.7.1 Discriminant Constraints

1   A discriminant_constraint specifies the values of the discriminants for a
given discriminated type.


                         Language Design Principles

        1.a   The rules in this clause are intentionally parallel to those
        given in Record Aggregates.

                                   Syntax

2   discriminant_constraint ::=
       (discriminant_association {, discriminant_association})

3   discriminant_association ::=
       [discriminant_selector_name {| discriminant_selector_name} =>] expression

    4   {named discriminant association} A discriminant_association is said
    to be named if it has one or more discriminant_selector_names;
    {positional discriminant association} it is otherwise said to be
    positional.  In a discriminant_constraint, any positional associations
    shall precede any named associations.


                            Name Resolution Rules

5   Each selector_name of a named discriminant_association shall resolve to
denote a discriminant of the subtype being constrained; {associated
discriminants (of a named discriminant_association)} the discriminants so
named are the associated discriminants of the named association.  {associated
discriminants (of a positional discriminant_association)} For a positional
association, the associated discriminant is the one whose discriminant_
specification occurred in the corresponding position in the known_
discriminant_part that defined the discriminants of the subtype being
constrained.

6   {expected type [discriminant_association expression]} The expected type
for the expression in a discriminant_association is that of the associated
discriminant(s).


                               Legality Rules

7   A discriminant_constraint is only allowed in a subtype_indication whose
subtype_mark denotes either an unconstrained discriminated subtype, or an
unconstrained access subtype whose designated subtype is an unconstrained
discriminated subtype.

8   A named discriminant_association with more than one selector_name is
allowed only if the named discriminants are all of the same type.  A
discriminant_constraint shall provide exactly one value for each discriminant
of the subtype being constrained.

9   The expression associated with an access discriminant shall be of a type
convertible to the anonymous access type.  {convertible [required]}

        9.a   Ramification:  This implies both convertibility of designated
        types, and static accessibility.  This implies that if an object of
        type T with an access discriminant is created by an allocator for an
        access type A, then it requires that the type of the expression
        associated with the access discriminant have an accessibility level
        that is not statically deeper than that of A. This is to avoid
        dangling references.  {94-4715.a}


                              Dynamic Semantics

10   {compatibility [discriminant constraint with a subtype]} A discriminant_
constraint is compatible with an unconstrained discriminated subtype if each
discriminant value belongs to the subtype of the corresponding discriminant.

        10.a   Ramification:  The "dependent compatibility check" has been
        eliminated in Ada 9X.  Any checking on subcomponents is performed
        when (and if) an object is created.

        10.b   Discussion:  There is no need to define compatibility with a
        constrained discriminated subtype, because one is not allowed to
        constrain it again.

11   {satisfies [a discriminant constraint]} A composite value satisfies a
discriminant constraint if and only if each discriminant of the composite
value has the value imposed by the discriminant constraint.

12   {elaboration [discriminant_constraint]} For the elaboration of a
discriminant_constraint, the expressions in the discriminant_associations are
evaluated in an arbitrary order and converted to the type of the associated
discriminant (which might raise Constraint_Error -- see 4.6); the expression
of a named association is evaluated (and converted) once for each associated
discriminant.  {implicit subtype conversion [discriminant values]} The result
of each evaluation and conversion is the value imposed by the constraint for
the associated discriminant.

        12.a   Reason:  We convert to the type, not the subtype, so that the
        definition of compatibility of discriminant constraints is not
        vacuous.


     NOTES
13   (54) The rules of the language ensure that a discriminant of an object
     always has a value, either from explicit or implicit initialization.

   13.a   Discussion:  Although it is illegal to constrain a class-wide
        tagged subtype, it is possible to have a partially constrained
        class-wide subtype: If the subtype S is defined by T(A => B), then
        S'Class is partially constrained in the sense that objects of subtype
        S'Class have to have discriminants corresponding to A equal to B, but
        there can be other discriminants defined in extensions that are not
        constrained to any particular value.


                                  Examples

14   Examples (using types declared above in clause 3.7):

15  Large   : Buffer(200);  --  constrained, always 200 characters
                            --   (explicit discriminant value)
    Message : Buffer;       --  unconstrained, initially 100 characters
                            --   (default discriminant value)
    Basis   : Square(5);    --  constrained, always 5 by 5
    Illegal : Square;       --  illegal, a Square has to be constrained


                         Inconsistencies With Ada 83

        15.a   {inconsistencies with Ada 83} Dependent compatibility checks
        are no longer performed on subtype declaration.  Instead they are
        deferred until object creation (see 3.3.1).  This is upward
        compatible for a program that does not raise Constraint_Error.

                         Wording Changes From Ada 83

        15.b   Everything in RM83-3.7.2(7-12), which specifies the initial
        values for discriminants, is now redundant with 3.3.1, 6.4.1, 8.5.1,
        and 12.4.  Therefore, we don't repeat it here.  Since the material is
        largely intuitive, but nevertheless complicated to state formally, it
        doesn't seem worth putting it in a "NOTE."



3.7.2 Operations of Discriminated Types

1   [If a discriminated type has default_expressions for its discriminants,
then unconstrained variables of the type are permitted, and the discriminants
of such a variable can be changed by assignment to the variable.  For a
formal parameter of such a type, an attribute is provided to determine
whether the corresponding actual parameter is constrained or unconstrained.]


                              Static Semantics

2   For a prefix A that is of a discriminated type [(after any implicit
dereference)], the following attribute is defined:

3   A'Constrained
                Yields the value True if A denotes a constant, a value, or a
                constrained variable, and False otherwise.

3.a     Implementation Note:  This attribute is primarily used on parameters,
        to determine whether the discriminants can be changed as part of an
        assignment.  The Constrained attribute is statically True for in
        parameters.  For in out and out parameters of a discriminated type,
        the value of this attribute needs to be passed as an implicit
        parameter, in general.  However, if the type does not have defaults
        for its discriminants, the attribute is statically True, so no
        implicit parameter is needed.  Parameters of a limited type with
        defaulted discriminants need this implicit parameter, unless there
        are no nonlimited views, because they might be passed to a subprogram
        whose body has visibility on a nonlimited view of the type, and hence
        might be able to assign to the object and change its discriminants.


                             Erroneous Execution

4   {erroneous execution} The execution of a construct is erroneous if the
construct has a constituent that is a name denoting a subcomponent that
depends on discriminants, and the value of any of these discriminants is
changed by this execution between evaluating the name and the last use
(within this execution) of the subcomponent denoted by the name.
        4.a   Ramification:  This rule applies to assignment_statements,
        calls (except when the discriminant-dependent subcomponent is an in
        parameter passed by copy), indexed_components, and slices.  Ada 83
        only covered the first two cases.  AI-00585 pointed out the situation
        with the last two cases.  The cases of object_renaming_declarations
        and generic formal in out objects are handled differently, by
        disallowing the situation at compile time.


                            Extensions to Ada 83

        4.b   {extensions to Ada 83} For consistency with other attributes,
        we are allowing the prefix of Constrained to be a value as well as an
        object of a discriminated type, and also an implicit dereference.
        These extensions are not important capabilities, but there seems no
        reason to make this attribute different from other similar
        attributes.  We are curious what most Ada 83 compilers do with
        F(1).X'Constrained.

        4.c   We now handle in a general way the cases of erroneousness
        identified by AI-585, where the prefix of an indexed_component or
        slice is discriminant-dependent, and the evaluation of the index or
        discrete range changes the value of a discriminant.

                         Wording Changes From Ada 83

        4.d   We have moved all discussion of erroneous use of names that
        denote discriminant-dependent subcomponents to this subclause.  In
        Ada 83, it used to appear separately under assignment_statements and
        subprogram calls.



3.8 Record Types

1   {record} {record type} A record object is a composite object consisting
of named components.  The value of a record object is a composite value
consisting of the values of the components.  {structure: see record type}


                                   Syntax

2   record_type_definition ::= [[abstract] tagged] [limited] record_definition

3   record_definition ::=
        record
           component_list
        end record
      | null record

4   component_list ::=
          component_item {component_item}
       | {component_item} variant_part
       |  null;

5   component_item ::= component_declaration | representation_clause

6   component_declaration ::=
       defining_identifier_list : component_definition [:= default_expression];


                            Name Resolution Rules

7   {expected type [component_declaration default_expression]} The expected
type for the default_expression, if any, in a component_declaration is the
type of the component.


                               Legality Rules

8   A default_expression is not permitted if the component is of a limited
type.

9   {components [of a record type]} Each component_declaration declares a
component of the record type.  Besides components declared by component_
declarations, the components of a record type include any components declared
by discriminant_specifications of the record type declaration.  [The
identifiers of all components of a record type shall be distinct.]

        9.a   Proof:  The identifiers of all components of a record type have
        to be distinct because they are all declared immediately within the
        same declarative region.  See Section 8.

10   Within a type_declaration, a name that denotes a component, protected
subprogram, or entry of the type is allowed only in the following cases:
{94-4663.a} {94-4664.a}

   11  A name that denotes any component, protected subprogram, or entry
       is allowed within a representation item that occurs within the
       declaration of the composite type.

   12  A name that denotes a noninherited discriminant is allowed within
       the declaration of the type, but not within the discriminant_
       part.  If the discriminant is used to define the constraint of a
       component, the bounds of an entry family, or the constraint of
       the parent subtype in a derived_type_definition then its name
       shall appear alone as a direct_name (not as part of a larger
       expression or expanded name).

 12.a   Reason:  This restriction simplifies implementation, and allows
        the outer discriminant and the inner discriminant or bound to
        possibly share storage.

 12.b   Ramification:  Other rules prevent such a discriminant from
        being an inherited one.

       A discriminant shall not be used to define the constraint of a
       scalar component.

 12.c   Reason:  This restriction is inherited from Ada 83.  The
        restriction is not really necessary from a language design point
        of view, but we did not remove it, in order to avoid unnecessary
        changes to existing compilers.

 12.d   Discussion:  Note that a discriminant can be used to define the
        constraint for a component that is of an access-to-composite
        type.

 12.e   Reason:  The above rules, and a similar one in 6.1 for formal
        parameters, are intended to allow initializations of components
        or parameters to occur in an arbitrary order -- whatever order
        is most efficient, since one default_expression cannot depend on
        the value of another one.  It also prevent circularities.

 12.f   Ramification:  Inherited discriminants are not allowed to be
        denoted, except within representation items.  However, the
        discriminant_selector_name of the parent subtype_indication is
        allowed to denote a discriminant of the parent.

13   If the name of the current instance of a type (see 8.6) is used to
define the constraint of a component, then it shall appear as a direct_name
that is the prefix of an attribute_reference whose result is of an access
type, and the attribute_reference shall appear alone.

        13.a   Reason:  This rule allows T'Access or T'Unchecked_Access, but
        disallows, for example, a range constraint (1..T'Size).  Allowing
        things like (1..T'Size) would mean that a per-object constraint could
        affect the size of the object, which would be bad.


                              Static Semantics

14   {nominal subtype [of a record component]} The component_definition of a
component_declaration defines the (nominal) subtype of the component.  If the
reserved word aliased appears in the component_definition, then the component
is aliased (see 3.10).

        14.a   Ramification:  In this case, the nominal subtype cannot be an
        unconstrained discriminated subtype.  See 3.6.

15   {null record} If the component_list of a record type is defined by the
reserved word null and there are no discriminants, then the record type has
no components and all records of the type are null records.  A record_
definition of null record is equivalent to record null; end record.

        15.a   Ramification:  This short-hand is available both for declaring
        a record type and a record extension -- see 3.9.1.


                              Dynamic Semantics

16   {elaboration [record_type_definition]} The elaboration of a record_type_
definition creates the record type and its first subtype, and consists of the
elaboration of the record_definition.  {elaboration [record_definition]} The
elaboration of a record_definition consists of the elaboration of its
component_list, if any.

17   {elaboration [component_list]} The elaboration of a component_list
consists of the elaboration of the component_items and variant_part, if any,
in the order in which they appear.  {elaboration [component_declaration]} The
elaboration of a component_declaration consists of the elaboration of the
component_definition.

        17.a   Discussion:  If the defining_identifier_list has more than one
        defining_identifier, we presume here that the transformation
        explained in 3.3.1 has already taken place.  Alternatively, we could
        say that the component_definition is elaborated once for each
        defining_identifier in the list.

18   {per-object expression} {per-object constraint} {entry index subtype}
Within the definition of a composite type, if a component_definition or
discrete_subtype_definition (see 9.5.2) includes a name that denotes a
discriminant of the type, or that is an attribute_reference whose prefix
denotes the current instance of the type, the expression containing the name
is called a per-object expression, and the constraint being defined is called
a per-object constraint.

        18.a   Discussion:  The evaluation of other expressions that appear
        in component_definitions and discrete_subtype_definitions is per-
        formed when the type definition is elaborated.  The evaluation of
        expressions that appear as default_expressions is postponed until an
        object is created.  Expressions in representation items that appear
        within a composite type definition are evaluated according to the
        rules of the particular representation item.

{elaboration [component_definition]} For the elaboration of a component_
definition of a component_declaration, if the constraint of the subtype_
indication is not a per-object constraint, then the subtype_indication is
elaborated.  On the other hand, if the constraint is a per-object constraint,
then the elaboration consists of the evaluation of any included expression
that is not part of a per-object expression.


     NOTES
19   (55) A component_declaration with several identifiers is equivalent to a
     sequence of single component_declarations, as explained in 3.3.1.

20   (56) The default_expression of a record component is only evaluated upon
     the creation of a default-initialized object of the record type
     (presuming the object has the component, if it is in a variant_part --
     see 3.3.1).

21   (57) The subtype defined by a component_definition (see 3.6) has to be a
     definite subtype.

22   (58) If a record type does not have a variant_part, then the same
     components are present in all values of the type.

23   (59) A record type is limited if it has the reserved word limited in its
     definition, or if any of its components are limited (see 7.5).

24   (60) {predefined operations [of a record type]} The predefined
     operations of a record type include membership tests, qualification, and
     explicit conversion.  If the record type is nonlimited, they also
     include assignment and the predefined equality operators.

25   (61) A component of a record can be named with a selected_component.  A
     value of a record can be specified with a record_aggregate, unless the
     record type is limited.


                                  Examples

26   Examples of record type declarations:

27  type Date is
       record
          Day   : Integer range 1 .. 31;
          Month : Month_Name;
          Year  : Integer range 0 .. 4000;
       end record;

28  type Complex is
       record
          Re : Real := 0.0;
          Im : Real := 0.0;
       end record;

29   Examples of record variables:

30  Tomorrow, Yesterday : Date;
    A, B, C : Complex;

31  -- both components of A, B, and C are implicitly initialized to zero


                            Extensions to Ada 83

        31.a   {extensions to Ada 83} The syntax rule for component_
        declaration is modified to use component_definition (instead of
        component_subtype_definition).  The effect of this change is to allow
        the reserved word aliased before the component_subtype_definition.

        31.b   A short-hand is provided for defining a null record type (and
        a null record extension), as these will be more common for abstract
        root types (and derived types without additional components).

        31.c   The syntax rule for record_type_definition is modified to
        allow the reserved words tagged and limited.  Tagging is new.
        Limitedness is now orthogonal to privateness.  In Ada 83 the syntax
        implied that limited private was sort of more private than private.
        However, limitedness really has nothing to do with privateness;
        limitedness simply indicates the lack of assignment capabilities, and
        makes perfect sense for nonprivate types such as record types.

                         Wording Changes From Ada 83

        31.d   The syntax rules now allow representation_clauses to appear in
        a record_definition.  This is not a language extension, because
        Legality Rules prevent all language-defined representation clauses
        from appearing there.  However, an implementation-defined attribute_
        definition_clause could appear there.  The reason for this change is
        to allow the rules for representation_clauses and representation
        pragmas to be as similar as possible.



3.8.1 Variant Parts and Discrete Choices

1   A record type with a variant_part specifies alternative lists of
components.  Each variant defines the components for the value or values of
the discriminant covered by its discrete_choice_list.

        1.a   Discussion:  {cover a value [distributed]} Discrete_choice_
        lists and discrete_choices are said to cover values as defined below;
        which discrete_choice_list covers a value determines which of various
        alternatives is chosen.  These are used in variant_parts, array_
        aggregates, and case_statements.


                         Language Design Principles

        1.b   The definition of ``cover'' in this subclause and the rules
        about discrete choices are designed so that they are also appropriate
        for array aggregates and case statements.

        1.c   The rules of this subclause intentionally parallel those for
        case statements.

                                   Syntax

2   variant_part ::=
       case discriminant_direct_name is
           variant
          {variant}
       end case;

3   variant ::=
       when discrete_choice_list =>
          component_list

4   discrete_choice_list ::= discrete_choice {| discrete_choice}

5   discrete_choice ::= expression | discrete_range | others


                            Name Resolution Rules

6   {discriminant (of a variant_part)} The discriminant_direct_name shall
resolve to denote a discriminant (called the discriminant of the variant_
part) specified in the known_discriminant_part of the full_type_declaration
that contains the variant_part.  {expected type [variant_part discrete_
choice]} The expected type for each discrete_choice in a variant is the type
of the discriminant of the variant_part.

        6.a   Ramification:  A full_type_declaration with a variant_part has
        to have a (new) known_discriminant_part; the discriminant of the
        variant_part cannot be an inherited discriminant.


                               Legality Rules

7   The discriminant of the variant_part shall be of a discrete type.

        7.a   Ramification:  It shall not be of an access type, named or
        anonymous.

8   The expressions and discrete_ranges given as discrete_choices in a
variant_part shall be static.  The discrete_choice others shall appear alone
in a discrete_choice_list, and such a discrete_choice_list, if it appears,
shall be the last one in the enclosing construct.

9   {cover a value [by a discrete_choice]} A discrete_choice is defined to
cover a value in the following cases:

   10  A discrete_choice that is an expression covers a value if the
       value equals the value of the expression converted to the
       expected type.

   11  A discrete_choice that is a discrete_range covers all values
       (possibly none) that belong to the range.

   12  The discrete_choice others covers all values of its expected type
       that are not covered by previous discrete_choice_lists of the
       same construct.

 12.a   Ramification:  For case_statements, this includes values outside
        the range of the static subtype (if any) to be covered by the
        choices.  It even includes values outside the base range of the
        case expression's type, since values of numeric types (and
        undefined values of any scalar type?)  can be outside their base
        range.

13   {cover a value [by a discrete_choice_list]} A discrete_choice_list
covers a value if one of its discrete_choices covers the value.

14   The possible values of the discriminant of a variant_part shall be
covered as follows:

   15  If the discriminant is of a static constrained scalar subtype,
       then each non-others discrete_choice shall cover only values in
       that subtype, and each value of that subtype shall be covered by
       some discrete_choice [(either explicitly or by others)];

   16  If the type of the discriminant is a descendant of a generic
       formal scalar type then the variant_part shall have an others
       discrete_choice;

 16.a   Reason:  The base range is not known statically in this case.

   17  Otherwise, each value of the base range of the type of the
       discriminant shall be covered [(either explicitly or by others)].

18   Two distinct discrete_choices of a variant_part shall not cover the same
value.


                              Static Semantics
19   If the component_list of a variant is specified by null, the variant has
no components.

20   {govern a variant_part} {govern a variant} The discriminant of a
variant_part is said to govern the variant_part and its variants.  In
addition, the discriminant of a derived type governs a variant_part and its
variants if it corresponds (see 3.7) to the discriminant of the variant_part.


                              Dynamic Semantics

21   A record value contains the values of the components of a particular
variant only if the value of the discriminant governing the variant is
covered by the discrete_choice_list of the variant.  This rule applies in
turn to any further variant that is, itself, included in the component_list
of the given variant.

22   {elaboration [variant_part]} The elaboration of a variant_part consists
of the elaboration of the component_list of each variant in the order in
which they appear.


                                  Examples

23   Example of record type with a variant part:

24  type Device is (Printer, Disk, Drum);
    type State  is (Open, Closed);

25  type Peripheral(Unit : Device := Disk) is
       record
          Status : State;
          case Unit is
             when Printer =>
                Line_Count : Integer range 1 .. Page_Size;
             when others =>
                Cylinder   : Cylinder_Index;
                Track      : Track_Number;
             end case;
          end record;

26   Examples of record subtypes:

27  subtype Drum_Unit is Peripheral(Drum);
    subtype Disk_Unit is Peripheral(Disk);

28   Examples of constrained record variables:

29  Writer   : Peripheral(Unit  => Printer);
    Archive  : Disk_Unit;


                            Extensions to Ada 83

        29.a   {extensions to Ada 83} In Ada 83, the discriminant of a
        variant_part is not allowed to be of a generic formal type.  This
        restriction is removed in Ada 9X; an others discrete_choice is
        required in this case.

                         Wording Changes From Ada 83

        29.b   The syntactic category choice is removed.  The syntax rules
        for variant, array_aggregate, and case_statement now use discrete_
        choice_list or discrete_choice instead.  The syntax rule for record_
        aggregate now defines its own syntax for named associations.

        29.c   We have added the term Discrete Choice to the title since this
        is where they are talked about.  This is analogous to the name of the
        subclause "Index Constraints and Discrete Ranges" in the clause on
        Array Types.

        29.d   The rule requiring that the discriminant denote a discriminant
        of the type being defined seems to have been left implicit in RM83.



3.9 Tagged Types and Type Extensions

1   [{dispatching operation [partial]} {polymorphism} {dynamic binding: see
dispatching operation} {generic unit: see also dispatching operation}
{variant: see also tagged type} Tagged types and type extensions support
object-oriented programming, based on inheritance with extension and run-time
polymorphism via dispatching operations.  {object-oriented programming (OOP):
see tagged types and type extensions} {OOP (object-oriented programming): see
tagged types and type extensions} {inheritance: see also tagged types and
type extension}]


                         Language Design Principles

        1.a   The intended implementation model is for a tag to be
        represented as a pointer to a statically allocated and link-time
        initialized type descriptor.  The type descriptor contains the
        address of the code for each primitive operation of the type.  It
        probably also contains other information, such as might make
        membership tests convenient and efficient.

        1.b   The primitive operations of a tagged type are known at its
        first freezing point; the type descriptor is laid out at that point.
        It contains linker symbols for each primitive operation; the linker
        fills in the actual addresses.

        1.c   Other implementation models are possible.

        1.d   The rules ensure that ``dangling dispatching'' is impossible;
        that is, when a dispatching call is made, there is always a body to
        execute.  This is different from some other object-oriented
        languages, such as Smalltalk, where it is possible to get a run-time
        error from a missing method.

        1.e   Dispatching calls should be efficient, and should have a
        bounded worst-case execution time.  This is important in a language
        intended for real-time applications.  In the intended implementation
        model, a dispatching call involves calling indirect through the
        appropriate slot in the dispatch table.  No complicated "method
        lookup" is involved.

        1.f   The programmer should have the choice at each call site of a
        dispatching operation whether to do a dispatching call or a
        statically determined call (i.e. whether the body executed should be
        determined at run time or at compile time).

        1.g   The same body should be executed for a call where the tag is
        statically determined to be T'Tag as for a dispatching call where the
        tag is found at run time to be T'Tag.  This allows one to test a
        given tagged type with statically determined calls, with some
        confidence that run-time dispatching will produce the same behavior.

        1.h   All views of a type should share the same type descriptor and
        the same tag.

        1.i   The visibility rules determine what is legal at compile time;
        they have nothing to do with what bodies can be executed at run time.
        Thus, it is possible to dispatch to a subprogram whose declaration is
        not visible at the call site.  In fact, this is one of the primary
        facts that gives object-oriented programming its power.  The
        subprogram that ends up being dispatched to by a given call might
        even be designed long after the call site has been coded and
        compiled.

        1.j   Given that Ada has overloading, determining whether a given
        subprogram overrides another is based both on the names and the type
        profiles of the operations.

        1.k   When a type extension is declared, if there is any place within
        its immediate scope where a certain subprogram of the parent is
        visible, then a matching subprogram should override.  If there is no
        such place, then a matching subprogram should be totally unrelated,
        and occupy a different slot in the type descriptor.  This is
        important to preserve the privacy of private parts; when an operation
        declared in a private part is inherited, the inherited version can be
        overridden only in that private part, in the package body, and in any
        children of the package.

        1.l   If an implementation shares code for instances of generic
        bodies, it should be allowed to share type descriptors of tagged
        types declared in the generic body, so long as they are not
        extensions of types declared in the specification of the generic
        unit.

                              Static Semantics

2   {tagged type} A record type or private type that has the reserved word
tagged in its declaration is called a tagged type.  [When deriving from a
tagged type, additional components may be defined.  As for any derived type,
additional primitive subprograms may be defined, and inherited primitive
subprograms may be overridden.]  {type extension} {extension (of a type)} The
derived type is called an extension of the ancestor type, or simply a type
extension.  {extension (of a record type)} {private extension} {extension (of
a private type)} Every type extension is also a tagged type, and is either a
record extension or a private extension of some other tagged type.  A record
extension is defined by a derived_type_definition with a record_extension_
part.  A private extension, which is a partial view of a record extension,
can be declared in the visible part of a package (see 7.3) or in a generic
formal part (see 12.5.1).

        2.a   Glossary entry:  {Tagged type} The objects of a tagged type
        have a run-time type tag, which indicates the specific type with
        which the object was originally created.  An operand of a class-wide
        tagged type can be used in a dispatching call; the tag indicates
        which subprogram body to invoke.  Nondispatching calls, in which the
        subprogram body to invoke is determined at compile time, are also
        allowed.  Tagged types may be extended with additional components.

        2.b   Ramification:  If a tagged type is declared other than in a
        package_specification, it is impossible to add new primitive
        subprograms for that type, although it can inherit primitive
        subprograms, and those can be overridden.  If the user incorrectly
        thinks a certain subprogram is primitive when it is not, and tries to
        call it with a dispatching call, an error message will be given at
        the call site.

        2.c   Note that the accessibility rules imply that a tagged type
        declared in a library package_specification cannot be extended in a
        nested subprogram or task body.

3   {tag of an object} An object of a tagged type has an associated
(run-time) tag that identifies the specific tagged type used to create the
object originally.  [The tag of an operand of a class-wide tagged type
T'Class controls which subprogram body is to be executed when a primitive
subprogram of type T is applied to the operand (see 3.9.2); {dispatching}
using a tag to control which body to execute is called dispatching.]  {type
tag: see tag} {run-time type: see tag} {type: see also tag} {class: see also
tag}

4   The tag of a specific tagged type identifies the full_type_declaration of
the type.  If a declaration for a tagged type occurs within a generic_
package_declaration, then the corresponding type declarations in distinct
instances of the generic package are associated with distinct tags.  For a
tagged type that is local to a generic package body, the language does not
specify whether repeated instantiations of the generic body result in
distinct tags.

        4.a   Reason:  This eases generic code sharing.

        4.b   Implementation Note:  The language does not specify whether
        repeated elaborations of the same full_type_declaration correspond to
        distinct tags.  In most cases, we expect that all elaborations will
        correspond to the same tag, since the tag will frequently be the
        address (or index) of a statically allocated type descriptor.
        However, with shared generics, the type descriptor might have to be
        allocated on a per-instance basis, which in some implementation
        models implies per-elaboration of the instantiation.

5   The following language-defined library package exists:

6   package Ada.Tags is
        type Tag is private;

7       function Expanded_Name(T : Tag) return String;
        function External_Tag(T : Tag) return String;
        function Internal_Tag(External : String) return Tag;

8       Tag_Error : exception;

9   private
       ... -- not specified by the language
    end Ada.Tags;

        9.a   Reason:  Tag is a nonlimited, definite subtype, because it
        needs the equality operators, so that tag checking makes sense.
        Also, equality, assignment, and object declaration are all useful
        capabilities for this subtype.

        9.b   For an object X and a type T, ``X'Tag = T'Tag'' is not needed,
        because a membership test can be used.  However, comparing the tags
        of two objects cannot be done via membership.  This is one reason to
        allow equality for type Tag.

10   The function Expanded_Name returns the full expanded name of the first
subtype of the specific type identified by the tag, in upper case, starting
with a root library unit.  The result is implementation defined if the type
is declared within an unnamed block_statement.

        10.a   To be honest:  This name, as well as each prefix of it, does
        not denote a renaming_declaration.

        10.b   Implementation defined:  The result of Tags.Expanded_Name for
        types declared within an unnamed block_statement.

11   The function External_Tag returns a string to be used in an external
representation for the given tag.  The call External_Tag(S'Tag) is equivalent
to the attribute_reference S'External_Tag (see 13.3).

        11.a   Reason:  It might seem redundant to provide both the function
        External_Tag and the attribute External_Tag.  The function is needed
        because the attribute can't be applied to values of type Tag.  The
        attribute is needed so that it can be specifiable via an attribute_
        definition_clause.

12   The function Internal_Tag returns the tag that corresponds to the given
external tag, or raises Tag_Error if the given string is not the external tag
for any specific type of the partition.

13   For every subtype S of a tagged type T (specific or class-wide), the
following attributes are defined:

14  S'Class
                S'Class denotes a subtype of the class-wide type (called
                T'Class in this International Standard) for the class rooted
                at T (or if S already denotes a class-wide subtype, then
                S'Class is the same as S).

                15   {unconstrained (subtype)} {constrained (subtype)}
                S'Class is unconstrained.  However, if S is constrained, then
                the values of S'Class are only those that when converted to
                the type T belong to S.

15.a    Ramification:  This attribute is defined for both specific and
        class-wide subtypes.  The definition is such that S'Class'Class is
        the same as S'Class.

15.b    Note that if S is constrained, S'Class is only partially constrained,
        since there might be additional discriminants added in descendants of
        T which are not constrained.

15.c    Reason:  The Class attribute is not defined for untagged subtypes
        (except for incomplete types and private types whose full view is
        tagged -- see 3.10.1 and 7.3.1) so as to preclude implicit conversion
        in the absence of run-time type information.  If it were defined for
        untagged subtypes, it would correspond to the concept of universal
        types provided for the predefined numeric classes.

16  S'Tag
                S'Tag denotes the tag of the type T (or if T is class-wide,
                the tag of the root type of the corresponding class).  The
                value of this attribute is of type Tag.

16.a    Reason:  S'Class'Tag equals S'Tag, to avoid generic contract model
        problems when S'Class is the actual type associated with a generic
        formal derived type.

17   Given a prefix X that is of a class-wide tagged type [(after any
implicit dereference)], the following attribute is defined:

18  X'Tag
                X'Tag denotes the tag of X. The value of this attribute is of
                type Tag.

18.a    Reason:  X'Tag is not defined if X is of a specific type.  This is
        primarily to avoid confusion that might result about whether the Tag
        attribute should reflect the tag of the type of X, or the tag of
        X. No such confusion is possible if X is of a class-wide type.


                              Dynamic Semantics

19   The tag associated with an object of a tagged type is determined as
follows:

   20  {tag of an object [stand-alone object, component, or aggregate]}
       The tag of a stand-alone object, a component, or an aggregate of
       a specific tagged type T identifies T.

 20.a   Discussion:  The tag of a formal parameter of type T is not
        necessarily the tag of T, if, for example, the actual was a type
        conversion.

   21  {tag of an object [object created by an allocator]} The tag of an
       object created by an allocator for an access type with a specific
       designated tagged type T, identifies T.

 21.a   Discussion:  The tag of an object designated by a value of such
        an access type might not be T, if, for example, the access value
        is the result of a type conversion.

   22  {tag of an object [class-wide object]} The tag of an object of a
       class-wide tagged type is that of its initialization expression.

 22.a   Ramification:  The tag of an object (even a class-wide one)
        cannot be changed after it is initialized, since a
        ``class-wide'' assignment_statement raises Constraint_Error if
        the tags don't match, and a ``specific'' assignment_statement
        does not affect the tag.

   23  {tag of an object [returned by a function]} The tag of the result
       returned by a function whose result type is a specific tagged
       type T identifies T.

 23.a   Implementation Note:  This requires a run-time check for limited
        tagged types, since they are returned "by-reference."  For a
        nonlimited type, a new anonymous object with the appropriate tag
        is created as part of the function return, and then assigned the
        value of the return expression.  See 6.5, ``Return Statements''.

   24  {tag of an object [returned by a function]} The tag of the result
       returned by a function with a class-wide result type is that of
       the return expression.

25   {tag of an object [preserved by type conversion and parameter passing]}
The tag is preserved by type conversion and by parameter passing.  The tag of
a value is the tag of the associated object (see 6.2).  {94-4774.a}
{94-4842.a}


                         Implementation Permissions

26   The implementation of the functions in Ada.Tags may raise Tag_Error if
no specific type corresponding to the tag passed as a parameter exists in the
partition at the time the function is called.

        26.a   Reason:  In most implementations, repeated elaborations of the
        same type_declaration will all produce the same tag.  In such an
        implementation, Tag_Error will be raised in cases where the internal
        or external tag was passed from a different partition.  However, some
        implementations might create a new tag value at run time for each
        elaboration of a type_declaration.  In that case, Tag_Error could
        also be raised if the created type no longer exists because the
        subprogram containing it has returned, for example.  We don't require
        the latter behavior; hence the word ``may'' in this rule.


     NOTES
27   (62) A type declared with the reserved word tagged should normally be
     declared in a package_specification, so that new primitive subprograms
     can be declared for it.

28   (63) Once an object has been created, its tag never changes.

29   (64) Class-wide types are defined to have unknown discriminants (see
     3.7).  This means that objects of a class-wide type have to be
     explicitly initialized (whether created by an object_declaration or an
     allocator), and that aggregates have to be explicitly qualified with a
     specific type when their expected type is class-wide.

30   (65) If S denotes an untagged private type whose full type is tagged,
     then S'Class is also allowed before the full type definition, but only
     in the private part of the package in which the type is declared (see
     7.3.1).  Similarly, the Class attribute is defined for incomplete types
     whose full type is tagged, but only within the library unit in which the
     incomplete type is declared (see 3.10.1).


                                  Examples

31   Examples of tagged record types:

32  type Point is tagged
      record
        X, Y : Real := 0.0;
      end record;

33  type Expression is tagged null record;
      -- Components will be added by each extension


                            Extensions to Ada 83

        33.a   {extensions to Ada 83} Tagged types are a new concept.



3.9.1 Type Extensions

1   [{type extension} {extension (of a type)} {record extension} {extension
(of a record type)} {private extension} {extension (of a private type)} Every
type extension is a tagged type, and is either a record extension or a
private extension of some other tagged type.]


                         Language Design Principles

        1.a   We want to make sure that we can extend a generic formal tagged
        type, without knowing its discriminants.

        1.b   We don't want to allow components in an extension aggregate to
        depend on discriminants inherited from the parent value, since such
        dependence requires staticness in aggregates, at least for variants.

                                   Syntax

2   record_extension_part ::= with record_definition


                               Legality Rules

3   The parent type of a record extension shall not be a class-wide type.  If
the parent type is nonlimited, then each of the components of the record_
extension_part shall be nonlimited.  {accessibility rule [record extension]}
The accessibility level (see 3.10.2) of a record extension shall not be
statically deeper than that of its parent type.  {94-4715.a} {generic
contract issue [partial]} In addition to the places where Legality Rules
normally apply (see 12.3), these rules apply also in the private part of an
instance of a generic unit.

        3.a   Reason:  If the parent is a limited formal type, then the
        actual might be nonlimited.

        3.b   A similar accessibility rule is not needed for private
        extensions, because in a package, the rule will apply to the full_
        type_declaration, and for a generic formal private extension, the
        actual is all that matters.

4   A type extension shall not be declared in a generic body if the parent
type is declared outside that body.

        4.a   Reason:  This paragraph ensures that a dispatching call will
        never attempt to execute an inaccessible subprogram body.

        4.b   The part about generic bodies is necessary in order to preserve
        the contract model.

        4.c   Since a generic unit can be instantiated at a deeper
        accessibility level than the generic unit, it is necessary to prevent
        type extensions whose parent is declared outside the generic unit.
        The same is true if the parent is a formal of the generic unit.  If
        the parent is declared in the generic_declaration (but is not a
        formal), we don't run afoul of the accessibility rules, because we
        know that the instance declaration and body will be at the same
        accessibility level.  However, we still have a problem in that case,
        because it might have an unknown number of abstract subprograms, as
        in the following example:

4.d         package P is
                type T is tagged null record;
                function F return T; -- Inherited versions will be abstract.
            end P;

4.e         generic
                type TT is tagged private;
            package Gp is
                type NT is abstract new TT with null record;
                procedure Q(X : in NT) is abstract;
            end Gp;

4.f         package body Gp is
                type NT2 is new NT with null record; -- Illegal!
                procedure Q(X : in NT2) is begin null; end Q;
                -- Is this legal or not?  Can't decide because
                -- we don't know whether TT had any functions that go abstract
                -- on extension.
            end Gp;

4.g         package I is new Gp(TT => P.T);

        4.h   I.NT is an abstract type with two abstract subprograms:  F
        (inherited as abstract) and Q (explicitly declared as abstract).  But
        the generic body doesn't know about F, so we don't know that it needs
        to be overridden to make a nonabstract extension of NT.  Furthermore,
        a formal tagged limited private type can be extended with limited
        components, but the actual might not be limited, which would allow
        assignment of limited types, which is bad.  Hence, we have to
        disallow this case as well.

        4.i   If TT were declared as abstract, then we could have the same
        problem with abstract procedures.

        4.j   We considered disallowing all tagged types in a generic body,
        for simplicity.  We decided not to go that far, in order to avoid
        unnecessary restrictions.

        4.k   {accessibility rule [not part of generic contract]} We also
        considered trying make the accessibility level part of the contract;
        i.e. invent some way of saying (in the generic_declaration) ``all
        instances of this generic unit will have the same accessibility level
        as the generic_declaration.''  Unfortunately, that doesn't solve the
        part of the problem having to do with abstract types.

        4.l   Children of generic units obviate the need for extension in the
        body somewhat.


                              Dynamic Semantics

5   {elaboration [record_extension_part]} The elaboration of a record_
extension_part consists of the elaboration of the record_definition.


     NOTES
6    (66) The term ``type extension'' refers to a type as a whole.  The term
     ``extension part'' refers to the piece of text that defines the
     additional components (if any) the type extension has relative to its
     specified ancestor type.

   6.a   Discussion:  We considered other terminology, such as ``extended
        type.''  However, the terms ``private extended type'' and ``record
        extended type'' did not convey the proper meaning.  Hence, we have
        chosen to uniformly use the term ``extension'' as the type resulting
        from extending a type, with ``private extension'' being one produced
        by privately extending the type, and ``record extension'' being one
        produced by extending the type with an additional record-like set of
        components.  Note also that the term ``type extension'' refers to the
        result of extending a type in the language Oberon as well (though
        there the term ``extended type'' is also used, interchangeably,
        perhaps because Oberon doesn't have the concept of a ``private
        extension'').

7    (67) The accessibility rules imply that a tagged type declared in a
     library package_specification can be extended only at library level or
     as a generic formal.  When the extension is declared immediately within
     a package_body, primitive subprograms are inherited and are overridable,
     but new primitive subprograms cannot be added.

8    (68) A name that denotes a component (including a discriminant) of the
     parent type is not allowed within the record_extension_part.  Similarly,
     a name that denotes a component defined within the record_extension_part
     is not allowed within the record_extension_part.  It is permissible to
     use a name that denotes a discriminant of the record extension,
     providing there is a new known_discriminant_part in the enclosing type
     declaration.  (The full rule is given in 3.8.)

   8.a   Reason:  The restriction against depending on discriminants of the
        parent is to simplify the definition of extension aggregates.  The
        restriction against using parent components in other ways is
        methodological; it presumably simplifies implementation as well.

9    (69) Each visible component of a record extension has to have a unique
     name, whether the component is (visibly) inherited from the parent type
     or declared in the record_extension_part (see 8.3).


                                  Examples

10   Examples of record extensions (of types defined above in 3.9):
{94-4514.a}

11  type Painted_Point is new Point with
      record
        Paint : Color := White;
      end record;
        -- Components X and Y are inherited

12  Origin : constant Painted_Point := (X | Y => 0.0, Paint => Black);

13  type Literal is new Expression with
      record                 -- a leaf in an Expression tree
        Value : Real;
      end record;

14  type Expr_Ptr is access all Expression'Class;
                                   -- see 3.10

15  type Binary_Operation is new Expression with
      record                 -- an internal node in an Expression tree
        Left, Right : Expr_Ptr;
      end record;

16  type Addition is new Binary_Operation with null record;
    type Subtraction is new Binary_Operation with null record;
      -- No additional components needed for these extensions

17  Tree : Expr_Ptr :=         -- A tree representation of ``5.0 + (13.0-7.0)''
       new Addition'(
          Left  => new Literal'(Value => 5.0),
          Right => new Subtraction'(
             Left  => new Literal'(Value => 13.0),
             Right => new Literal'(Value => 7.0)));


                            Extensions to Ada 83

        17.a   {extensions to Ada 83} Type extension is a new concept.



3.9.2 Dispatching Operations of Tagged Types

1   {dispatching operation [distributed]} {dispatching call (on a dispatching
operation)} {nondispatching call (on a dispatching operation)} {statically
determined tag} {dynamically determined tag} {polymorphism} {run-time
polymorphism} {controlling tag (for a call on a dispatching operation)} The
primitive subprograms of a tagged type are called dispatching operations.  [A
dispatching operation can be called using a statically determined controlling
tag, in which case the body to be executed is determined at compile time.
Alternatively, the controlling tag can be dynamically determined, in which
case the call dispatches to a body that is determined at run time;] such a
call is termed a dispatching call.  [As explained below, the properties of
the operands and the context of a particular call on a dispatching operation
determine how the controlling tag is determined, and hence whether or not the
call is a dispatching call.  Run-time polymorphism is achieved when a
dispatching operation is called by a dispatching call.]  {object-oriented
programming (OOP): see dispatching operations of tagged types} {OOP
(object-oriented programming): see dispatching operations of tagged types}
{message: see dispatching call} {method: see dispatching subprogram} {virtual
function: see dispatching subprogram}


                         Language Design Principles

        1.a   The controlling tag determination rules are analogous to the
        overload resolution rules, except they deal with run-time type
        identification (tags) rather than compile-time type resolution.  As
        with overload resolution, controlling tag determination may depend on
        operands or result context.

                              Static Semantics

2   {call on a dispatching operation} {dispatching operation} A call on a
dispatching operation is a call whose name or prefix denotes the declaration
of a primitive subprogram of a tagged type, that is, a dispatching operation.

        2.a   Ramification:  This definition implies that a call through the
        dereference of an access-to-subprogram value is never considered a
        call on a dispatching operation.  Note also that if the prefix
        denotes a renaming_declaration, the place where the renaming occurs
        determines whether it is primitive; the thing being renamed is
        irrelevant.

{controlling operand} A controlling operand in a call on a dispatching
operation of a tagged type T is one whose corresponding formal parameter is
of type T or is of an anonymous access type with designated type T;
{controlling formal parameter} the corresponding formal parameter is called a
controlling formal parameter.  If the controlling formal parameter is an
access parameter, the controlling operand is the object designated by the
actual parameter, rather than the actual parameter itself.  {controlling
result} If the call is to a (primitive) function with result type T, then the
call has a controlling result -- the context of the call can control the
dispatching.

3   A name or expression of a tagged type is either statically tagged,
dynamically tagged, or tag indeterminate, according to whether, when used as
a controlling operand, the tag that controls dispatching is determined
statically by the operand's (specific) type, dynamically by its tag at run
time, or from context.  A qualified_expression or parenthesized expression is
statically, dynamically, or indeterminately tagged according to its operand.
For other kinds of names and expressions, this is determined as follows:

    4  {statically tagged} The name or expression is statically tagged
       if it is of a specific tagged type and, if it is a call with a
       controlling result, it has at least one statically tagged
       controlling operand;

 4.a    Discussion:  It is illegal to have both statically tagged and
        dynamically tagged controlling operands in the same call -- see
        below.

    5  {dynamically tagged} The name or expression is dynamically tagged
       if it is of a class-wide type, or it is a call with a controlling
       result and at least one dynamically tagged controlling operand;

    6  {tag indeterminate} The name or expression is tag indeterminate
       if it is a call with a controlling result, all of whose
       controlling operands (if any) are tag indeterminate.

7   [A type_conversion is statically or dynamically tagged according to
whether the type determined by the subtype_mark is specific or class-wide,
respectively.]  For a controlling operand that is designated by an actual
parameter, the controlling operand is statically or dynamically tagged
according to whether the designated type of the actual parameter is specific
or class-wide, respectively.

        7.a   Ramification:  A type_conversion is never tag indeterminate,
        even if its operand is.  A designated object is never tag
        indeterminate.


                               Legality Rules

8   A call on a dispatching operation shall not have both dynamically tagged
and statically tagged controlling operands.

        8.a   Reason:  This restriction is intended to minimize confusion
        between whether the dynamically tagged operands are implicitly
        converted to, or tag checked against the specific type of the
        statically tagged operand(s).

9   If the expected type for an expression or name is some specific tagged
type, then the expression or name shall not be dynamically tagged unless it
is a controlling operand in a call on a dispatching operation.  Similarly, if
the expected type for an expression is an anonymous access-to-specific tagged
type, then the expression shall not be of an access-to-class-wide type unless
it designates a controlling operand in a call on a dispatching operation.

        9.a   Reason:  This prevents implicit "truncation" of a
        dynamically-tagged value to the specific type of the target
        object/formal.  An explicit conversion is required to request this
        truncation.

        9.b   Ramification:  This rule applies to all expressions or names
        with a specific expected type, not just those that are actual
        parameters to a dispatching call.  This rule does not apply to a
        membership test whose expression is class-wide, since any type that
        covers the tested type is explicitly allowed.  See 4.5.2.

10   In the declaration of a dispatching operation of a tagged type,
everywhere a subtype of the tagged type appears as a subtype of the profile
(see 6.1), it shall statically match the first subtype of the tagged type.
{statically matching [required]} If the dispatching operation overrides an
inherited subprogram, it shall be subtype conformant with the inherited
subprogram.  {subtype conformance (required)} A dispatching operation shall
not be of convention Intrinsic.  {94-4774.b} If a dispatching operation
overrides the predefined equals operator, then it shall be of convention Ada
[(either explicitly or by default -- see 6.3.1)].

        10.a   Reason:  These rules ensure that constraint checks can be
        performed by the caller in a dispatching call, and parameter passing
        conventions match up properly.  A special rule on aggregates prevents
        values of a tagged type from being created that are outside of its
        first subtype.

11   The default_expression for a controlling formal parameter of a
dispatching operation shall be tag indeterminate.  A controlling formal
parameter that is an access parameter shall not have a default_expression.

        11.a   Reason:  The first part ensures that the default_expression
        always produces the "correct" tag when called with or without
        dispatching, or when inherited by a descendant.  If it were
        statically tagged, the default would be useless for a dispatching
        call; if it were dynamically tagged, the default would be useless for
        a nondispatching call.

        11.b   The second part is consistent with the first part, since
        designated objects are never tag-indeterminate.

12   A given subprogram shall not be a dispatching operation of two or more
distinct tagged types.

        12.a   Reason:  This restriction minimizes confusion since multiple
        dispatching is not provided.  The normal solution is to replace all
        but one of the tagged types with their class-wide types.

13   The explicit declaration of a primitive subprogram of a tagged type
shall occur before the type is frozen (see 13.14).  [For example, new
dispatching operations cannot be added after objects or values of the type
exist, nor after deriving a record extension from it, nor after a body.]

        13.a   Change:  Rule moved here from 13.14, ``Freezing Rules'', as
        per WG9 resolution.
        13.b   Reason:  This rule is needed because (1) we don't want people
        dispatching to things that haven't been declared yet, and (2) we want
        to allow tagged type descriptors to be static (allocated statically,
        and initialized to link-time-known symbols).  Suppose T2 inherits
        primitive P from T1, and then overrides P. Suppose P is called before
        the declaration of the overriding P. What should it dispatch to?  If
        the answer is the new P, we've violated the first principle above.
        If the answer is the old P, we've violated the second principle.  (A
        call to the new one necessarily raises Program_Error, but that's
        beside the point.)

        13.c   Note that a call upon a dispatching operation of type T will
        freeze T.

        13.d   We considered applying this rule to all derived types, for
        uniformity.  However, that would be upward incompatible, so we
        rejected the idea.  As in Ada 83, for an untagged type, the above
        call upon P will call the old P (which is arguably confusing).

        13.e   Implementation Note:  Because of this rule, the type
        descriptor can be created (presumably containing linker symbols
        pointing at the not-yet-compiled bodies) at the first freezing point
        of the type.  It also prevents, for a tagged type declared in a
        package_specification, overriding in the body or by a child
        subprogram.

        13.f   Ramification:  A consequence is that for a derived_type_
        declaration in a declarative_part, only the first primitive
        subprogram can be declared by a subprogram_body.


                              Dynamic Semantics

14   {execution [call on a dispatching operation]} {controlling tag value}
For the execution of a call on a dispatching operation of a type T, the
controlling tag value determines which subprogram body is executed.  The
controlling tag value is defined as follows:

   15  {statically determined tag [partial]} If one or more controlling
       operands are statically tagged, then the controlling tag value is
       statically determined to be the tag of T.

   16  If one or more controlling operands are dynamically tagged, then
       the controlling tag value is not statically determined, but is
       rather determined by the tags of the controlling operands.  {Tag_
       Check [partial]} {check, language-defined (Tag_Check)} If there
       is more than one dynamically tagged controlling operand, a check
       is made that they all have the same tag.  {Constraint_Error
       (raised by failure of run-time check)} If this check fails,
       Constraint_Error is raised unless the call is a function_call
       whose name denotes the declaration of an equality operator
       (predefined or user defined) that returns Boolean, in which case
       the result of the call is defined to indicate inequality, and no
       subprogram_body is executed.  This check is performed prior to
       evaluating any tag-indeterminate controlling operands.

 16.a   Reason:  Tag mismatch is considered an error (except for "=" and
        "/=") since the corresponding primitive subprograms in each
        specific type expect all controlling operands to be of the same
        type.  For tag mismatch with an equality operator, rather than
        raising an exception, "=" returns False and "/=" returns True.
        No equality operator is actually invoked, since there is no
        common tag value to control the dispatch.  Equality is a special
        case to be consistent with the existing Ada 83 principle that
        equality comparisons, even between objects with different
        constraints, never raise Constraint_Error.

   17  If all of the controlling operands are tag-indeterminate, then:

          18  If the call has a controlling result and is itself a
              (possibly parenthesized or qualified) controlling operand
              of an enclosing call on a dispatching operation of type T,
              then its controlling tag value is determined by the
              controlling tag value of this enclosing call;

          19  {statically determined tag [partial]} Otherwise, the
              controlling tag value is statically determined to be the
              tag of type T.

 19.a   Ramification:  This includes the cases of a tag-indeterminate
        procedure call, and a tag-indeterminate function_call that is
        used to initialize a class-wide formal parameter or class-wide
        object.

20   For the execution of a call on a dispatching operation, the body
executed is the one for the corresponding primitive subprogram of the
specific type identified by the controlling tag value.  The body for an
explicitly declared dispatching operation is the corresponding explicit body
for the subprogram.  The body for an implicitly declared dispatching
operation that is overridden is the body for the overriding subprogram, [even
if the overriding occurs in a private part.]  The body for an inherited
dispatching operation that is not overridden is the body of the corresponding
subprogram of the parent or ancestor type.

        20.a   To be honest:  In the unusual case in which a dispatching
        subprogram is explicitly declared (overridden) by a body (with no
        preceding subprogram_declaration), the body for that dispatching
        subprogram is that body; that is, the ``corresponding explicit body''
        in the above rule is the body itself.

        20.b   Reason:  The wording of the above rule is intended to ensure
        that the same body is executed for a given tag, whether that tag is
        determined statically or dynamically.  For a type declared in a
        package, it doesn't matter whether a given subprogram is overridden
        in the visible part or the private part, and it doesn't matter
        whether the call is inside or outside the package.  {94-5001.b} For
        example:

20.c        package P1 is
                type T1 is tagged null record;
                procedure Op_A(Arg : in T1);
                procedure Op_B(Arg : in T1);
            end P1;

20.d        with P1; use P1;
            package P2 is
                type T2 is new T1 with null record;
                procedure Op_A(Param : in T2);
            private
                procedure Op_B(Param : in T2);
            end P2;

20.e        with P1; with P2;
            procedure Main is
                X : T2;
                Y : T1'Class := X;
            begin
                P2.Op_A(Param => X); -- Nondispatching call.
                P1.Op_A(Arg => Y); -- Dispatching call.
                P2.Op_B(Arg => X); -- Nondispatching call.
                P1.Op_B(Arg => Y); -- Dispatching call.
            end Main;

        20.f   The two calls to Op_A both execute the body of Op_A that has
        to occur in the body of package P2.  Similarly, the two calls to Op_B
        both execute the body of Op_B that has to occur in the body of
        package P2, even though Op_B is overridden in the private part of P2.
        Note, however, that the formal parameter names are different for
        P2.Op_A versus P2.Op_B.  The overriding declaration for P2.Op_B is
        not visible in Main, so the name in the call actually denotes the
        implicit declaration of Op_B inherited from T1.

        20.g   If a call occurs in the program text before an overriding,
        which can happen only if the call is part of a default expression,
        the overriding will still take effect for that call.  {94-4457.a}
        {94-4814.a}

        20.h   Implementation Note:  Even when a tag is not statically
        determined, a compiler might still be able to figure it out and
        thereby avoid the overhead of run-time dispatching.


     NOTES
21   (70) The body to be executed for a call on a dispatching operation is
     determined by the tag; it does not matter whether that tag is determined
     statically or dynamically, and it does not matter whether the
     subprogram's declaration is visible at the place of the call.
     {94-4457.a} {94-4814.a}

22   (71) This subclause covers calls on primitive subprograms of a tagged
     type.  Rules for tagged type membership tests are described in 4.5.2.
     Controlling tag determination for an assignment_statement is described
     in 5.2.

23   (72) A dispatching call can dispatch to a body whose declaration is not
     visible at the place of the call.

24   (73) A call through an access-to-subprogram value is never a dispatching
     call, even if the access value designates a dispatching operation.
     Similarly a call whose prefix denotes a subprogram_renaming_declaration
     cannot be a dispatching call unless the renaming itself is the
     declaration of a primitive subprogram.


                            Extensions to Ada 83

        24.a   {extensions to Ada 83} The concept of dispatching operations
        is new.



3.9.3 Abstract Types and Subprograms

1   [{abstract type} {abstract data type (ADT): see also abstract type} {ADT
(abstract data type): see also abstract type} {concrete type: see nonabstract
type} An abstract type is a tagged type intended for use as a parent type for
type extensions, but which is not allowed to have objects of its own.
{abstract subprogram} {concrete subprogram: see nonabstract subprogram} An
abstract subprogram is a subprogram that has no body, but is intended to be
overridden at some point when inherited.  Because objects of an abstract type
cannot be created, a dispatching call to an abstract subprogram always
dispatches to some overriding body.]


                         Language Design Principles

        1.a   An abstract subprogram has no body, so the rules in this clause
        are designed to ensure (at compile time) that the body will never be
        invoked.  We do so primarily by disallowing the creation of values of
        the abstract type.  Therefore, since type conversion and parameter
        passing don't change the tag, we know we will never get a class-wide
        value with a tag identifying an abstract type.  This means that we
        only have to disallow nondispatching calls on abstract subprograms
        (dispatching calls will never reach them).

                               Legality Rules

2   {abstract type} {type (abstract)} An abstract type is a specific type
that has the reserved word abstract in its declaration.  Only a tagged type
is allowed to be declared abstract.

        2.a   Ramification:  Untagged types are never abstract, even though
        they can have primitive abstract subprograms.  Such subprograms
        cannot be called, unless they also happen to be dispatching
        operations of some tagged type, and then only via a dispatching call.

        2.b   Class-wide types are never abstract.  If T is abstract, then it
        is illegal to declare a stand-alone object of type T, but it is OK to
        declare a stand-alone object of type T'Class; the latter will get a
        tag from its initial value, and this tag will necessarily be
        different from T'Tag.

3   {abstract subprogram} {subprogram (abstract)} A subprogram declared by an
abstract_subprogram_declaration (see 6.1) is an abstract subprogram.  If it
is a primitive subprogram of a tagged type, then the tagged type shall be
abstract.

        3.a   Ramification:  Note that for a private type, this applies to
        both views.  The following is illegal:

3.b         package P is
                type T is abstract tagged private;
                function Foo (X : T) return Boolean is abstract; -- Illegal!
            private
                type T is tagged null record; -- Illegal!
                X : T;
                Y : Boolean := Foo (T'Class (X));
            end P;

        3.c   The full view of T is not abstract, but has an abstract
        operation Foo, which is illegal.  The two lines marked "-- Illegal!"
        are illegal when taken together.  {94-4936.a} {94-4949.a}

        3.d   Reason:  We considered disallowing untagged types from having
        abstract primitive subprograms.  However, we rejected that plan,
        because it introduced some silly anomalies, and because such
        subprograms are harmless (if not terribly useful).  For example:

3.e         package P is
               type Field_Size is range 0..100;
               type T is abstract tagged null record;
               procedure Print(X : in T; F : in Field_Size := 0) is abstract;
              . . .
            package Q is
               type My_Field_Size is new Field_Size;
               -- implicit declaration of Print(X : T; F : My_Field_Size := 0) \
is abstract;
            end Q;

        3.f   It seemed silly to make the derivative of My_Field_Size
        illegal, just because there was an implicitly declared abstract
        subprogram that was not primitive on some tagged type.  Other rules
        could be formulated to solve this problem, but the current ones seem
        like the simplest.

4   For a derived type, if the parent or ancestor type has an abstract
primitive subprogram, or a primitive function with a controlling result,
then:

    5  If the derived type is abstract or untagged, the inherited
       subprogram is abstract.

 5.a    Ramification:  Note that it is possible to override a concrete
        subprogram with an abstract one.

    6  Otherwise, the subprogram shall be overridden with a nonabstract
       subprogram; [for a type declared in the visible part of a
       package, the overriding may be either in the visible or the
       private part.]  However, if the type is a generic formal type,
       the subprogram need not be overridden for the formal type itself;
       [a nonabstract version will necessarily be provided by the actual
       type.]  {94-4833.a} {94-4834.a}

 6.a    Reason:  A function that returns the parent type becomes
        abstract for an abstract type extension (if not overridden)
        because conversion from a parent type to a type extension is not
        defined, and function return semantics is defined in terms of
        conversion.  (Note that parameters of mode in out or out do not
        have this problem, because the tag of the actual is not
        changed.)

 6.b    Note that the overriding required above can be in the private
        part, which allows the following:

6.c         package Pack1 is
                type Ancestor is abstract ...;
                procedure Do_Something(X : in Ancestor) is abstract;
            end Pack1;

6.d         with Pack1; use Pack1;
            package Pack2 is
                type T1 is new Ancestor with record ...;
                    -- A concrete type.
                procedure Do_Something(X : in T1); -- Have to override.
            end Pack2;

6.e         with Pack1; use Pack1;
            with Pack2; use Pack2;
            package Pack3 is
                type T2 is new Ancestor with private;
                    -- A concrete type.
            private
                type T2 is new T1 with -- Parent different from ancestor.
                  record ... end record;
                -- Here, we inherit Pack2.Do_Something.
            end Pack3;

 6.f    T2 inherits an abstract Do_Something, but T is not abstract, so
        Do_Something has to be overridden.  However, it is OK to
        override it in the private part.  In this case, we override it
        by inheriting a concrete version from a different type.
        Nondispatching calls to Pack3.Do_Something are allowed both
        inside and outside package Pack3.

7   A call on an abstract subprogram shall be a dispatching call;
[nondispatching calls to an abstract subprogram are not allowed.]

        7.a   Ramification:  If an abstract subprogram is not a dispatching
        operation of some tagged type, then it cannot be called at all.

8   The type of an aggregate, or of an object created by an object_
declaration or an allocator, or a generic formal object of mode in, shall not
be abstract.  The type of the target of an assignment operation (see 5.2)
shall not be abstract.  The type of a component shall not be abstract.  If
the result type of a function is abstract, then the function shall be
abstract.

        8.a   Reason:  This ensures that values of an abstract type cannot be
        created, which ensures that a dispatching call to an abstract
        subprogram will not try to execute the nonexistent body.

        8.b   Generic formal objects of mode in are like constants; therefore
        they should be forbidden for abstract types.  Generic formal objects
        of mode in out are like renamings; therefore, abstract types are OK
        for them, though probably not terribly useful.

9   If a partial view is not abstract, the corresponding full view shall not
be abstract.  If a generic formal type is abstract, then for each primitive
subprogram of the formal that is not abstract, the corresponding primitive
subprogram of the actual shall not be abstract.

        9.a   Discussion:  By contrast, we allow the actual type to be
        nonabstract even if the formal type is declared abstract.  Hence, the
        most general formal tagged type possible is "type T(<>) is abstract
        tagged limited private;".

        9.b   For an abstract private extension declared in the visible part
        of a package, it is only possible for the full type to be nonabstract
        if the private extension has no abstract dispatching operations.

10   For an abstract type declared in a visible part, an abstract primitive
subprogram shall not be declared in the private part, unless it is overriding
an abstract subprogram implicitly declared in the visible part.  For a tagged
type declared in a visible part, a primitive function with a controlling
result shall not be declared in the private part, unless it is overriding a
function implicitly declared in the visible part.

        10.a   Reason:  The ``visible part'' could be that of a package or a
        generic package.  This rule is needed because a non-abstract type
        extension declared outside the package would not know about any
        abstract primitive subprograms or primitive functions with
        controlling results declared in the private part, and wouldn't know
        that they need to be overridden with non-abstract subprograms.  The
        rule applies to a tagged record type or record extension declared in
        a visible part, just as to a tagged private type or private
        extension.  The rule applies to explicitly and implicitly declared
        abstract subprograms:

10.b        package Pack is
                type T is abstract new T1 with private;
            private
                type T is abstract new T2 with record ... end record;
                ...
            end Pack;

        10.c   The above example would be illegal if T1 has a non-abstract
        primitive procedure P, but T2 overrides P with an abstract one; the
        private part should override P with a non-abstract version.  On the
        other hand, if the P were abstract for both T1 and T2, the example
        would be legal as is.

11   A generic actual subprogram shall not be an abstract subprogram.  The
prefix of an attribute_reference for the Access, Unchecked_Access, or Address
attributes shall not denote an abstract subprogram.

        11.a   Ramification:  An abstract_subprogram_declaration is not
        syntactically a subprogram_declaration.  Nonetheless, an abstract
        subprogram is a subprogram, and an abstract_subprogram_declaration is
        a declaration of a subprogram.

        11.b   The part about generic actual subprograms includes those given
        by default.


     NOTES
12   (74) Abstractness is not inherited; to declare an abstract type, the
     reserved word abstract has to be used in the declaration of the type
     extension.

   12.a   Ramification:  A derived type can be abstract even if its parent is
        not.  Similarly, an inherited concrete subprogram can be overridden
        with an abstract subprogram.

13   (75) A class-wide type is never abstract.  Even if a class is rooted at
     an abstract type, the class-wide type for the class is not abstract, and
     an object of the class-wide type can be created; the tag of such an
     object will identify some nonabstract type in the class.


                                  Examples

14   Example of an abstract type representing a set of natural numbers:

15  package Sets is
        subtype Element_Type is Natural;
        type Set is abstract tagged null record;
        function Empty return Set is abstract;
        function Union(Left, Right : Set) return Set is abstract;
        function Intersection(Left, Right : Set) return Set is abstract;
        function Unit_Set(Element : Element_Type) return Set is abstract;
        procedure Take(Element : out Element_Type; From : in out Set) is abstra\
ct;
    end Sets;


     NOTES
16   (76) Notes on the example:  Given the above abstract type, one could
     then derive various (nonabstract) extensions of the type, representing
     alternative implementations of a set.  One might use a bit vector, but
     impose an upper bound on the largest element representable, while
     another might use a hash table, trading off space for flexibility.

   16.a   Discussion:  One way to export a type from a package with some
        components visible and some components private is as follows:

16.b        package P is
                type Public_Part is abstract tagged
                    record
                        ...
                    end record;
                type T is new Public_Part with private;
                ...
            private
                type T is new Public_Part with
                    record
                        ...
                    end record;
            end P;

   16.c   The fact that Public_Part is abstract tells clients they have to
        create objects of type T instead of Public_Part.  Note that the
        public part has to come first; it would be illegal to declare a
        private type Private_Part, and then a record extension T of it,
        unless T were in the private part after the full declaration of
        Private_Part, but then clients of the package would not have
        visibility to T.



3.10 Access Types

1   {access type} {access value} {designate} A value of an access type (an
access value) provides indirect access to the object or subprogram it
designates.  Depending on its type, an access value can designate either
subprograms, objects created by allocators (see 4.8), or more generally
aliased objects of an appropriate type.  {pointer: see access value} {pointer
type: see access type}

        1.a   Discussion:  A name denotes an entity; an access value
        designates an entity.  The ``dereference'' of an access value X,
        written ``X.all'', is a name that denotes the entity designated by X.


                         Language Design Principles

        1.b   Access values should always be well defined (barring uses of
        certain unchecked features of Section 13).  In particular,
        uninitialized access variables should be prevented by compile-time
        rules.

                                   Syntax

2   access_type_definition ::=
        access_to_object_definition
      | access_to_subprogram_definition

3   access_to_object_definition ::=
        access [general_access_modifier] subtype_indication

4   general_access_modifier ::= all | constant

5   access_to_subprogram_definition ::=
        access [protected] procedure parameter_profile
      | access [protected] function  parameter_and_result_profile

6   access_definition ::= access subtype_mark


                              Static Semantics

7   {access-to-object type} {access-to-subprogram type} {pool-specific access
type} {general access type} There are two kinds of access types,
access-to-object types, whose values designate objects, and
access-to-subprogram types, whose values designate subprograms.  {storage
pool} Associated with an access-to-object type is a storage pool; several
access types may share the same storage pool.  {pool element} A storage pool
is an area of storage used to hold dynamically allocated objects (called pool
elements) created by allocators[; storage pools are described further in
13.11, ``Storage Management''].

8   {pool-specific access type} {general access type} Access-to-object types
are further subdivided into pool-specific access types, whose values can
designate only the elements of their associated storage pool, and general
access types, whose values can designate the elements of any storage pool, as
well as aliased objects created by declarations rather than allocators, and
aliased subcomponents of other objects.

        8.a   Implementation Note:  The value of an access type will
        typically be a machine address.  However, a value of a pool-specific
        access type can be represented as an offset (or index) relative to
        its storage pool, since it can point only to the elements of that
        pool.

9   {aliased} A view of an object is defined to be aliased if it is defined
by an object_declaration or component_definition with the reserved word
aliased, or by a renaming of an aliased view.  In addition, the dereference
of an access-to-object value denotes an aliased view, as does a view
conversion (see 4.6) of an aliased view.  Finally, the current instance of a
limited type, and a formal parameter or generic formal object of a tagged
type are defined to be aliased.  {94-4978.a} [Aliased views are the ones that
can be designated by an access value.]  {constrained (object)} {unconstrained
(object)} {constrained by its initial value} If the view defined by an
object_declaration is aliased, and the type of the object has discriminants,
then the object is constrained; if its nominal subtype is unconstrained, then
the object is constrained by its initial value.  [Similarly, if the object
created by an allocator has discriminants, the object is constrained, either
by the designated subtype, or by its initial value.]  {94-4858.a}

        9.a   Glossary entry:  {Aliased} An aliased view of an object is one
        that can be designated by an access value.  Objects allocated by
        allocators are aliased.  Objects can also be explicitly declared as
        aliased with the reserved word aliased.  The Access attribute can be
        used to create an access value designating an aliased object.

        9.b   Ramification:  The current instance of a nonlimited type is not
        aliased.

        9.c   The object created by an allocator is aliased, but not its
        subcomponents, except of course for those that themselves have
        aliased in their component_definition.

        9.d   The renaming of an aliased object is aliased.

        9.e   Slices are never aliased.  See 4.1.2 for more discussion.

        9.f   Reason:  The current instance of a limited type is defined to
        be aliased so that an access discriminant of a component can be
        initialized with T'Access inside the definition of T.

        9.g   A formal parameter of a tagged type is defined to be aliased so
        that a (tagged) parameter X may be passed to an access parameter P by
        using P => X'Access.  Access parameters are most important for tagged
        types because of dispatching-on-access-parameters (see 3.9.2).  By
        restricting this to formal parameters, we minimize problems
        associated with allowing components that are not declared aliased to
        be pointed-to from within the same record.

        9.h   A view conversion of an aliased view is aliased so that the
        type of an access parameter can be changed without first converting
        to a named access type.  For example:

9.i         type T1 is tagged ...;
            procedure P(X : access T1);

9.j         type T2 is new T1 with ...;
            procedure P(X : access T2) is
            begin
                P(T1(X.all)'Access);  -- hand off to T1's P
                . . .      -- now do extra T2-specific processing
            end P;

        9.k   The rule about objects with discriminants is necessary because
        values of a constrained access subtype can designate an object whose
        nominal subtype is unconstrained; without this rule, a check on every
        use of such values would be required to ensure that the discriminants
        of the object had not changed.  With this rule (among others), we
        ensure that if there might exist aliased views of a discriminated
        object, then the object is necessarily constrained.  Note that this
        rule is necessary only for untagged types, since a discriminant of a
        tagged type can't have a default, so all tagged discriminated objects
        are always constrained anyway.

        9.l   We considered making more kinds of objects aliased by default.
        In particular, any object of a by-reference type will pretty much
        have to be allocated at an addressable location, so it can be passed
        by reference without using bit-field pointers.  Therefore, one might
        wish to allow the Access and and Unchecked_Access attributes for such
        objects.  However, private parts are transparent to the definition of
        ``by-reference type'', so if we made all objects of a by-reference
        type aliased, we would be violating the privacy of private parts.
        Instead, we would have to define a concept of ``visibly
        by-reference'' and base the rule on that.  This seemed to complicate
        the rules more than it was worth, especially since there is no way to
        declare an untagged limited private type to be by-reference, since
        the full type might by nonlimited.

        9.m   Discussion:  Note that we do not use the term ``aliased'' to
        refer to formal parameters that are referenced through multiple
        access paths (see 6.2).

10   An access_to_object_definition defines an access-to-object type and its
first subtype; {designated subtype (of a named access type)} {designated type
(of a named access type)} the subtype_indication defines the designated
subtype of the access type.  If a general_access_modifier appears, then the
access type is a general access type.  {access-to-constant type} If the
modifier is the reserved word constant, then the type is an
access-to-constant type[; a designated object cannot be updated through a
value of such a type].  {access-to-variable type} If the modifier is the
reserved word all, then the type is an access-to-variable type[; a designated
object can be both read and updated through a value of such a type].  If no
general_access_modifier appears in the access_to_object_definition, the
access type is a pool-specific access-to-variable type.

        10.a   To be honest:  The type of the designated subtype is called
        the designated type.

        10.b   Reason:  The modifier all was picked to suggest that values of
        a general access type could point into ``all'' storage pools, as well
        as to objects declared aliased, and that ``all'' access (both read
        and update) to the designated object was provided.  We couldn't think
        of any use for pool-specific access-to-constant types, so any access
        type defined with the modifier constant is considered a general
        access type, and can point into any storage pool or at other
        (appropriate) aliased objects.

        10.c   Implementation Note:  The predefined generic Unchecked_
        Deallocation can be instantiated for any named access-to-variable
        type.  There is no (language-defined) support for deallocating
        objects designated by a value of an access-to-constant type.  Because
        of this, an allocator for an access-to-constant type can allocate out
        of a storage pool with no support for deallocation.  Frequently, the
        allocation can be done at link-time, if the size and initial value
        are known then.

        10.d   Discussion:  For the purpose of generic formal type matching,
        the relevant subclasses of access types are access-to-subprogram
        types, access-to-constant types, and (named) access-to-variable
        types, with its subclass (named) general access-to-variable types.
        Pool-specific access-to-variable types are not a separately matchable
        subclass of types, since they don't have any ``extra'' operations
        relative to all (named) access-to-variable types.

11   {access-to-subprogram type} An access_to_subprogram_definition defines
an access-to-subprogram type and its first subtype; {designated profile (of
an access-to-subprogram type)} the parameter_profile or parameter_and_result_
profile defines the designated profile of the access type.  {calling
convention (associated with a designated profile)} There is a calling
convention associated with the designated profile[; only subprograms with
this calling convention can be designated by values of the access type.]  By
default, the calling convention is ``protected'' if the reserved word
protected appears, and ``Ada'' otherwise.  [See Annex B for how to override
this default.]

        11.a   Ramification:  The calling convention protected is in italics
        to emphasize that it cannot be specified explicitly by the user.
        This is a consequence of it being a reserved word.

        11.b   Implementation Note:  For an access-to-subprogram type, the
        representation of an access value might include implementation-
        defined information needed to support up-level references -- for
        example, a static link.  The accessibility rules (see 3.10.2) ensure
        that in a "global-display-based" implementation model (as opposed to
        a static-link-based model), an access-to-(unprotected)-subprogram
        value need consist only of the address of the subprogram.  The global
        display is guaranteed to be properly set up any time the designated
        subprogram is called.  Even in a static-link-based model, the only
        time a static link is definitely required is for an
        access-to-subprogram type declared in a scope nested at least two
        levels deep within subprogram or task bodies, since values of such a
        type might designate subprograms nested a smaller number of levels.
        For the normal case of an access-to-subprogram type declared at the
        outermost (library) level, a code address by itself should be
        sufficient to represent the access value in many implementations.

        11.c   For access-to-protected-subprogram, the access values will
        necessarily include both an address (or other identification) of the
        code of the subprogram, as well as the address of the associated
        protected object.  This could be thought of as a static link, but it
        will be needed even for global-display-based implementation models.
        It corresponds to the value of the ``implicit parameter'' that is
        passed into every call of a protected operation, to identify the
        current instance of the protected type on which they are to operate.

        11.d   Any Elaboration_Check is performed when a call is made through
        an access value, rather than when the access value is first "created"
        via a 'Access.  For implementation models that normally put that
        check at the call-site, an access value will have to point to a
        separate entry point that does the check.  Alternatively, the access
        value could point to a "subprogram descriptor" that consisted of two
        words (or perhaps more), the first being the address of the code, the
        second being the elaboration bit.  Or perhaps more efficiently, just
        the address of the code, but using the trick that the descriptor is
        initialized to point to a Raise-Program-Error routine initially, and
        then set to point to the "real" code when the body is elaborated.

        11.e   For implementations that share code between generic
        instantiations, the extra level of indirection suggested above to
        support Elaboration_Checks could also be used to provide a pointer to
        the per-instance data area normally required when calling shared
        code.  The trick would be to put a pointer to the per-instance data
        area into the subprogram descriptor, and then make sure that the
        address of the subprogram descriptor is loaded into a "known"
        register whenever an indirect call is performed.  Once inside the
        shared code, the address of the per-instance data area can be
        retrieved out of the subprogram descriptor, by indexing off the
        "known" register.

        11.f   Essentially the same implementation issues arise for calls on
        dispatching operations of tagged types, except that the static link
        is always known "statically."

        11.g   Note that access parameters of an anonymous access-to-
        subprogram type are not permitted.  If there were such parameters,
        full ``downward'' closures would be required, meaning that in an
        implementation that uses a per-task (global) display, the display
        would have to be passed as a hidden parameter, and reconstructed at
        the point of call.  This was felt to be an undue implementation
        burden, given that an equivalent (actually, more general) capability
        is available via formal subprogram parameters to a generic.

12   {anonymous access type} {designated subtype (of an anonymous access
type)} {designated type (of an anonymous access type)} An access_definition
defines an anonymous general access-to-variable type; the subtype_mark
denotes its designated subtype.  [An access_definition is used in the
specification of an access discriminant (see 3.7) or an access parameter (see
6.1).]

13   {null value (of an access type)} For each (named) access type, there is
a literal null which has a null access value designating no entity at all.
[The null value of a named access type is the default initial value of the
type.]  Other values of an access type are obtained by evaluating an
attribute_reference for the Access or Unchecked_Access attribute of an
aliased view of an object or non-intrinsic subprogram, or, in the case of a
named access-to-object type, an allocator[, which returns an access value
designating a newly created object (see 3.10.2)].

        13.a   Ramification:  A value of an anonymous access type (that is,
        the value of an access parameter or access discriminant) cannot be
        null.

        13.b   Reason:  Access parameters allow dispatching on the tag of the
        object designated by the actual parameter (which gets converted to
        the anonymous access type as part of the call).  In order for
        dispatching to work properly, there had better be such an object.
        Hence, the type conversion will raise Constraint_Error if the value
        of the actual parameter is null.

14   {constrained [subtype]} {unconstrained [subtype]} [All subtypes of an
access-to-subprogram type are constrained.]  The first subtype of a type
defined by an access_type_definition or an access_to_object_definition is
unconstrained if the designated subtype is an unconstrained array or
discriminated type; otherwise it is constrained.

        14.a   Proof:  The Legality Rules on range_constraints (see 3.5) do
        not permit the subtype_mark of the subtype_indication to denote an
        access-to-scalar type, only a scalar type.  The Legality Rules on
        index_constraints (see 3.6.1) and discriminant_constraints (see
        3.7.1) both permit access-to-composite types in a subtype_indication
        with such _constraints.  Note that an access-to-access-to-composite
        is never permitted in a subtype_indication with a constraint.

        14.b   Reason:  Only composite_constraints are permitted for an
        access type, and only on access-to-composite types.  A constraint on
        an access-to-scalar or access-to-access type might be violated due to
        assignments via other access paths that were not so constrained.  By
        contrast, if the designated subtype is an array or discriminated
        type, the constraint could not be violated by unconstrained
        assignments, since array objects are always constrained, and aliased
        discriminated objects are also constrained (by fiat, see Static
        Semantics).


                              Dynamic Semantics

15   {compatibility [composite_constraint with an access subtype]} A
composite_constraint is compatible with an unconstrained access subtype if it
is compatible with the designated subtype.  {satisfies [for an access value]}
An access value satisfies a composite_constraint of an access subtype if it
equals the null value of its type or if it designates an object whose value
satisfies the constraint.

16   {elaboration [access_type_definition]} The elaboration of an access_
type_definition creates the access type and its first subtype.  For an
access-to-object type, this elaboration includes the elaboration of the
subtype_indication, which creates the designated subtype.

17   {elaboration [access_definition]} The elaboration of an access_
definition creates an anonymous general access-to-variable type [(this
happens as part of the initialization of an access parameter or access
discriminant)].


     NOTES
18   (77) Access values are called ``pointers'' or ``references'' in some
     other languages.

19   (78) Each access-to-object type has an associated storage pool; several
     access types can share the same pool.  An object can be created in the
     storage pool of an access type by an allocator (see 4.8) for the access
     type.  A storage pool (roughly) corresponds to what some other languages
     call a ``heap.''  See 13.11 for a discussion of pools.

20   (79) Only index_constraints and discriminant_constraints can be applied
     to access types (see 3.6.1 and 3.7.1).


                                  Examples

21   Examples of access-to-object types:

22  type Peripheral_Ref is access Peripheral;  --  see 3.8.1
    type Binop_Ptr is access all Binary_Operation'Class;
                                               -- general access-to-class-wide,\
 see 3.9.1

23   Example of an access subtype:

24  subtype Drum_Ref is Peripheral_Ref(Drum);  --  see 3.8.1

25   Example of an access-to-subprogram type:

26  type Message_Procedure is access procedure (M : in String := "Error!");
    procedure Default_Message_Procedure(M : in String);
    Give_Message : Message_Procedure := Default_Message_Procedure'Access;
    ...
    procedure Other_Procedure(M : in String);
    ...
    Give_Message := Other_Procedure'Access;
    ...
    Give_Message("File not found.");  -- call with parameter (.all is optional)
    Give_Message.all;                 -- call with no parameters


                            Extensions to Ada 83

        26.a   {extensions to Ada 83} The syntax for access_type_definition
        is changed to support general access types (including access-to-
        constants) and access-to-subprograms.  The syntax rules for general_
        access_modifier and access_definition are new.

                         Wording Changes From Ada 83

        26.b   We use the term "storage pool" to talk about the data area
        from which allocation takes place.  The term "collection" is no
        longer used.  ("Collection" and "storage pool" are not the same thing
        because multiple unrelated access types can share the same storage
        pool; see 13.11 for more discussion.)



3.10.1 Incomplete Type Declarations

1   There are no particular limitations on the designated type of an access
type.  In particular, the type of a component of the designated type can be
another access type, or even the same access type.  This permits mutually
dependent and recursive access types.  An incomplete_type_declaration can be
used to introduce a type to be used as a designated type, while deferring its
full definition to a subsequent full_type_declaration.


                                   Syntax

2   incomplete_type_declaration ::= type defining_identifier [discriminant_part\
];


                               Legality Rules

3   {requires a completion [incomplete_type_declaration]} An incomplete_type_
declaration requires a completion, which shall be a full_type_declaration.
[If the incomplete_type_declaration occurs immediately within either the
visible part of a package_specification or a declarative_part, then the full_
type_declaration shall occur later and immediately within this visible part
or declarative_part.  If the incomplete_type_declaration occurs immediately
within the private part of a given package_specification, then the full_type_
declaration shall occur later and immediately within either the private part
itself, or the declarative_part of the corresponding package_body.]

        3.a   Proof:  This is implied by the next AARM-only rule, plus the
        rules in 3.11.1, ``Completions of Declarations'' which require a
        completion to appear later and immediately within the same
        declarative region.

        3.b   To be honest:  If the incomplete_type_declaration occurs
        immediately within the visible part of a package_specification, then
        the full_type_declaration shall occur immediately within this visible
        part.

        3.c   To be honest:  If the implementation supports it, an
        incomplete_type_declaration can be completed by a pragma Import.

4   If an incomplete_type_declaration has a known_discriminant_part, then a
full_type_declaration that completes it shall have a fully conforming
(explicit) known_discriminant_part (see 6.3.1).  {full conformance
(required)} [If an incomplete_type_declaration has no discriminant_part (or
an unknown_discriminant_part), then a corresponding full_type_declaration is
nevertheless allowed to have discriminants, either explicitly, or inherited
via derivation.]

5   The only allowed uses of a name that denotes an incomplete_type_
declaration are as follows:

        5.a   Discussion:  No need to say "prior to the end of the full_type_
        declaration" since the name would not denote the incomplete_type_
        declaration after the end of the full_type_declaration.  Also, with
        child library units, it would not be well defined whether they come
        before or after the full_type_declaration for deferred incomplete
        types.

    6  as the subtype_mark in the subtype_indication of an access_to_
       object_definition; [the only form of constraint allowed in this
       subtype_indication is a discriminant_constraint;]

 6.a    Implementation Note:  We now allow discriminant_constraints even
        if the full type is deferred to the package body.  However,
        there is no particular implementation burden because we have
        dropped the concept of the dependent compatibility check.  In
        other words, we have effectively repealed AI-00007.

    7  as the subtype_mark defining the subtype of a parameter or result
       of an access_to_subprogram_definition; {94-4618.a}

 7.a    Reason:  This allows, for example, a record to have a component
        designating a subprogram that takes that same record type as a
        parameter.

    8  as the subtype_mark in an access_definition;

    9  as the prefix of an attribute_reference whose attribute_
       designator is Class; such an attribute_reference is similarly
       restricted to the uses allowed here; when used in this way, the
       corresponding full_type_declaration shall declare a tagged type,
       and the attribute_reference shall occur in the same library unit
       as the incomplete_type_declaration.

 9.a    Reason:  This is to prevent children from imposing requirements
        on their ancestor library units for deferred incomplete types.

10   A dereference (whether implicit or explicit -- see 4.1) shall not be of
an incomplete type.


                              Static Semantics

11   {incomplete type} An incomplete_type_declaration declares an incomplete
type and its first subtype; the first subtype is unconstrained if a known_
discriminant_part appears.

        11.a   Reason:  If an unknown_discriminant_part or no discriminant_
        part appears, then the constrainedness of the first subtype doesn't
        matter for any other rules or semantics, so we don't bother defining
        it.  The case with a known_discriminant_part is the only case in
        which a constraint could later be given in a subtype_indication
        naming the incomplete type.


                              Dynamic Semantics

12   {elaboration [incomplete_type_declaration]} The elaboration of an
incomplete_type_declaration has no effect.

        12.a   Reason:  An incomplete type has no real existence, so it
        doesn't need to be "created" in the usual sense we do for other
        types.  It is roughly equivalent to a "forward;" declaration in
        Pascal.  Private types are different, because they have a different
        set of characteristics from their full type.


     NOTES
13   (80) {completion legality [partial]} Within a declarative_part, an
     incomplete_type_declaration and a corresponding full_type_declaration
     cannot be separated by an intervening body.  This is because a type has
     to be completely defined before it is frozen, and a body freezes all
     types declared prior to it in the same declarative_part (see 13.14).


                                  Examples

14   Example of a recursive type:

15  type Cell;  --  incomplete type declaration
    type Link is access Cell;
16  type Cell is
       record
          Value  : Integer;
          Succ   : Link;
          Pred   : Link;
       end record;

17  Head   : Link  := new Cell'(0, null, null);
    Next   : Link  := Head.Succ;

18   Examples of mutually dependent access types:

19  type Person(<>);    -- incomplete type declaration
    type Car;           -- incomplete type declaration

20  type Person_Name is access Person;
    type Car_Name    is access all Car;

21  type Car is
       record
          Number  : Integer;
          Owner   : Person_Name;
       end record;

22  type Person(Sex : Gender) is
       record
          Name     : String(1 .. 20);
          Birth    : Date;
          Age      : Integer range 0 .. 130;
          Vehicle  : Car_Name;
          case Sex is
             when M => Wife           : Person_Name(Sex => F);
             when F => Husband        : Person_Name(Sex => M);
          end case;
       end record;

23  My_Car, Your_Car, Next_Car : Car_Name := new Car;  -- see 4.8
    George : Person_Name := new Person(M);
       ...
    George.Vehicle := Your_Car;


                            Extensions to Ada 83

        23.a   {extensions to Ada 83} The full_type_declaration that
        completes an incomplete_type_declaration may have a known_
        discriminant_part even if the incomplete_type_declaration does not.

        23.b   A discriminant_constraint may be applied to an incomplete
        type, even if it its completion is deferred to the package body,
        because there is no ``dependent compatibility check'' required any
        more.  Of course, the constraint can be specified only if a known_
        discriminant_part was given in the incomplete_type_declaration.  As
        mentioned in the previous paragraph, that is no longer required even
        when the full type has discriminants.

                         Wording Changes From Ada 83

        23.c   Dereferences producing incomplete types were not explicitly
        disallowed in RM83, though AI-00039 indicated that it was not
        strictly necessary since troublesome cases would result in
        Constraint_Error at run time, since the access value would
        necessarily be null.  However, this introduces an undesirable
        implementation burden, as illustrated by Example 4 of AI-00039:

23.d        package Pack is
                type Pri is private;
            private
                type Sep;
                type Pri is access Sep;
                X : Pri;
            end Pack;

23.e        package body Pack is -- Could be separately compiled!
                type Sep is ...;
                X := new Sep;
            end Pack;

23.f        pragma Elaborate(Pack);
            private package Pack.Child is
                I : Integer := X.all'Size; -- Legal, by AI-00039.
            end Pack.Child;

        23.g   Generating code for the above example could be a serious
        implementation burden, since it would require all aliased objects to
        store size dope, and for that dope to be in the same format for all
        kinds of types (or some other equivalently inefficient implemen-
        tation).  On the contrary, most implementations allocate dope
        differently (or not at all) for different designated subtypes.



3.10.2 Operations of Access Types

1   [The attribute Access is used to create access values designating aliased
objects and non-intrinsic subprograms.  The ``accessibility'' rules prevent
dangling references (in the absence of uses of certain unchecked features --
see Section 13).  ]{94-4715.a} {94-4570.a} {94-4724.a} {94-4725.a}
{94-4780.a}


                         Language Design Principles

        1.a   It should be possible for an access value to designate an
        object declared by an object declaration, or a subcomponent thereof.
        In implementation terms, this means pointing at stack-allocated and
        statically allocated data structures.  However, dangling references
        should be prevented, primarily via compile-time rules, so long as
        features like Unchecked_Access and Unchecked_Deallocation are not
        used.

        1.b   In order to create such access values, we require that the
        access type be a general access type, that the designated object be
        aliased, and that the accessibility rules be obeyed.

                            Name Resolution Rules

2   {expected type [access attribute_reference]} For an attribute_reference
with attribute_designator Access (or Unchecked_Access -- see 13.10), the
expected type shall be a single access type[; the prefix of such an
attribute_reference is never interpreted as an implicit_dereference].
{expected profile [Access attribute_reference prefix]} If the expected type
is an access-to-subprogram type, then the expected profile of the prefix is
the designated profile of the access type.

        2.a   Discussion:  Saying that the expected type shall be a "single
        access type" is our "new" way of saying that the type has to be
        determinable from context using only the fact that it is an access
        type.  See 4.2 and 8.6.  Specifying the expected profile only implies
        type conformance.  The more stringent subtype conformance is required
        by a Legality Rule.  This is the only Resolution Rule that applies to
        the name in a prefix of an attribute_reference.  In all other cases,
        the name has to be resolved without using context.  See 4.1.4.


                              Static Semantics

3   {accessibility level} {level (accessibility)} {deeper (accessibility
level)} {depth (accessibility level)} {dangling references (prevention via
accessibility rules)} {lifetime} [The accessibility rules, which prevent
dangling references, are written in terms of accessibility levels, which
reflect the run-time nesting of masters.  As explained in 7.6.1, a master is
the execution of a task_body, a block_statement, a subprogram_body, an entry_
body, or an accept_statement.  An accessibility level is deeper than another
if it is more deeply nested at run time.  {94-4746.} For example, an object
declared local to a called subprogram has a deeper accessibility level than
an object declared local to the calling subprogram.  The accessibility rules
for access types require that the accessibility level of an object designated
by an access value be no deeper than that of the access type.  This ensures
that the object will live at least as long as the access type, which in turn
ensures that the access value cannot later designate an object that no longer
exists.  The Unchecked_Access attribute may be used to circumvent the
accessibility rules.]

4   {statically deeper} {deeper (statically)} [A given accessibility level is
said to be statically deeper than another if the given level is known at
compile time (as defined below) to be deeper than the other for all possible
executions.  In most cases, accessibility is enforced at compile time by
Legality Rules.  Run-time accessibility checks are also used, since the
Legality Rules do not cover certain cases involving access parameters and
generic packages.]  {94-4857.a} {94-4918.a}

5   Each master, and each entity and view created by it, has an accessibility
level:

    6  The accessibility level of a given master is deeper than that of
       each dynamically enclosing master, and deeper than that of each
       master upon which the task executing the given master directly
       depends (see 9.3).

    7  An entity or view created by a declaration has the same
       accessibility level as the innermost enclosing master, except in
       the cases of renaming and derived access types described below.
       A parameter of a master has the same accessibility level as the
       master.

    8  The accessibility level of a view of an object or subprogram
       defined by a renaming_declaration is the same as that of the
       renamed view.

    9  The accessibility level of a view conversion is the same as that
       of the operand.  {94-4745.a}

   10  For a function whose result type is a return-by-reference type,
       the accessibility level of the result object is the same as that
       of the master that elaborated the function body.  For any other
       function, the accessibility level of the result object is that of
       the execution of the called function.

   11  The accessibility level of a derived access type is the same as
       that of its ultimate ancestor.

   12  The accessibility level of the anonymous access type of an access
       discriminant is the same as that of the containing object or
       associated constrained subtype.

   13  The accessibility level of the anonymous access type of an access
       parameter is the same as that of the view designated by the
       actual.  If the actual is an allocator, this is the accessibility
       level of the execution of the called subprogram.

   14  The accessibility level of an object created by an allocator is
       the same as that of the access type.

   15  The accessibility level of a view of an object or subprogram
       denoted by a dereference of an access value is the same as that
       of the access type.

   16  The accessibility level of a component, protected subprogram, or
       entry of (a view of) a composite object is the same as that of
       (the view of) the composite object.

17   {statically deeper} {deeper (statically)} One accessibility level is
defined to be statically deeper than another in the following cases:

   18  For a master that is statically nested within another master, the
       accessibility level of the inner master is statically deeper than
       that of the outer master.

 18.a   To be honest:  Strictly speaking, this should talk about the
        constructs (such as subprogram_bodies) being statically nested
        within one another; the masters are really the executions of
        those constructs.

 18.b   To be honest:  If a given accessibility level is statically
        deeper than another, then each level defined to be the same as
        the given level is statically deeper than each level defined to
        be the same as the other level.

   19  The statically deeper relationship does not apply to the
       accessibility level of the anonymous type of an access parameter;
       that is, such an accessibility level is not considered to be
       statically deeper, nor statically shallower, than any other.

   20  For determining whether one level is statically deeper than
       another when within a generic package body, the generic package
       is presumed to be instantiated at the same level as where it was
       declared; run-time checks are needed in the case of more deeply
       nested instantiations.  {94-4857.a} {94-4918.a}

   21  For determining whether one level is statically deeper than
       another when within the declarative region of a type_declaration,
       the current instance of the type is presumed to be an object
       created at a deeper level than that of the type.  {94-4857.b}
       {94-4927.a}

 21.a   Ramification:  In other words, the rules are checked at compile
        time of the type_declaration, in an assume-the-worst manner.

22   {library level} {level (library)} The accessibility level of all library
units is called the library level; a library-level declaration or entity is
one whose accessibility level is the library level.

        22.a   Ramification:  Library_unit_declarations are library level.
        Nested declarations are library level if they are nested only within
        packages (possibly more than one), and not within subprograms, tasks,
        etc.

        22.b   To be honest:  The definition of the accessibility level of
        the anonymous type of an access parameter cheats a bit, since it
        refers to the view designated by the actual, but access values
        designate objects, not views of objects.  What we really mean is the
        view that ``would be'' denoted by an expression ``X.all'', where X is
        the actual, even though such an expression is a figment of our
        imagination.  The definition is intended to be equivalent to the
        following more verbose version:  The accessibility level of the
        anonymous type of an access parameter is as follows:

         22.c  if the actual is an expression of a named access type --
               the accessibility level of that type;

         22.d  if the actual is an allocator -- the accessibility level
               of the execution of the called subprogram;

         22.e  if the actual is a reference to the Access attribute --
               the accessibility level of the view denoted by the
               prefix;

         22.f  if the actual is a reference to the Unchecked_Access
               attribute -- library accessibility level;

         22.g  if the actual is an access parameter -- the accessibility
               level of its type.

        22.h   Note that the allocator case is explicitly mentioned in the
        RM9X, because otherwise the definition would be circular:  the level
        of the anonymous type is that of the view designated by the actual,
        which is that of the access type.

        22.i   Discussion:  A deeper accessibility level implies a shorter
        maximum lifetime.  Hence, when a rule requires X to have a level that
        is ``not deeper than'' Y's level, this requires that X has a lifetime
        at least as long as Y. (We say ``maximum lifetime'' here, because the
        accessibility level really represents an upper bound on the lifetime;
        an object created by an allocator can have its lifetime prematurely
        ended by an instance of Unchecked_Deallocation.)

        22.j   Package elaborations are not masters, and are therefore
        invisible to the accessibility rules:  an object declared immediately
        within a package has the same accessibility level as an object
        declared immediately within the declarative region containing the
        package.  This is true even in the body of a package; it jibes with
        the fact that objects declared in a package_body live as long as
        objects declared outside the package, even though the body objects
        are not visible outside the package.

        22.k   Note that the level of the view denoted by X.all can be
        different from the level of the object denoted by X.all.  The former
        is determined by the type of X; the latter is determined either by
        the type of the allocator, or by the master in which the object was
        declared.  The former is used in several Legality Rules and run-time
        checks; the latter is used to define when X.all gets finalized.  The
        level of a view reflects what we can conservatively ``know'' about
        the object of that view; for example, due to type_conversions, an
        access value might designate an object that was allocated by an
        allocator for a different access type.

        22.l   Similarly, the level of the view denoted by X.all.Comp can be
        different from the level of the object denoted by X.all.Comp.

        22.m   If Y is statically deeper than X, this implies that Y will be
        (dynamically) deeper than X in all possible executions.

        22.n   Most accessibility checking is done at compile time; the rules
        are stated in terms of ``statically deeper than''.  The exceptions
        are:

         22.o  Checks involving access parameters.  The fact that
               ``statically deeper than'' is not defined for the
               anonymous access type of an access parameter implies that
               any rule saying ``shall not be statically deeper than''
               does not apply to such a type, nor to anything defined to
               have ``the same'' level as such a type.

         22.p  Checks involving entities and views within generic
               packages.  This is because an instantiation can be at a
               level that is more deeply nested than the generic package
               itself.  In implementations that use a macro-expansion
               model of generics, these violations can be detected at
               macro-expansion time.  For implementations that share
               generics, run-time code is needed to detect the error.

         22.q  Checks during function return.

        22.r   Note that run-time checks are not required for access
        discriminants, because their accessibility is determined statically
        by the accessibility level of the enclosing object.

        22.s   The accessibility level of the result object of a function
        reflects the time when that object will be finalized; we don't allow
        pointers to the object to survive beyond that time.  {94-4857.a}
        {94-4918.a}

        22.t   We sometimes use the terms ``accessible'' and ``inaccessible''
        to mean that something has an accessibility level that is not deeper,
        or deeper, respectively, than something else.

        22.u   Implementation Note:  If an accessibility Legality Rule is
        satisfied, then the corresponding run-time check (if any) cannot fail
        (and a reasonable implementation will not generate any checking code)
        unless access parameters or shared generic bodies are involved.

        22.v   Accessibility levels are defined in terms of the relations
        ``the same as'' and ``deeper than''.  To make the discussion more
        concrete, we can assign actual numbers to each level.  Here, we
        assume that library-level accessibility is level 0, and each level
        defined as ``deeper than'' is one level deeper.  Thus, a subprogram
        directly called from the environment task (such as the main
        subprogram) would be at level 1, and so on.

        22.w   Accessibility is not enforced at compile time for access
        parameters.  The ``obvious'' implementation of the run-time checks
        would be inefficient, and would involve distributed overhead;
        therefore, an efficient method is given below.  The ``obvious''
        implementation would be to pass the level of the caller at each
        subprogram call, task creation, etc.  This level would be incremented
        by 1 for each dynamically nested master.  An Accessibility_Check
        would be implemented as a simple comparison -- checking that X is not
        deeper than Y would involve checking that X <= Y.

        22.x   A more efficient method is based on passing static nesting
        levels (within constructs that correspond at run time to masters --
        packages don't count).  Whenever an access parameter is passed, an
        implicit extra parameter is passed with it.  The extra parameter
        represents (in an indirect way) the accessibility level of the
        anonymous access type, and, therefore, the level of the view denoted
        by a dereference of the access parameter.  This is analogous to the
        implicit ``Constrained'' bit associated with certain formal
        parameters of an unconstrained but definite composite subtype.  In
        this method, we avoid distributed overhead:  it is not necessary to
        pass any extra information to subprograms that have no access
        parameters.  For anything other than an access parameter and its
        anonymous type, the static nesting level is known at compile time,
        and is defined analogously to the RM9X definition of accessibility
        level (e.g. derived access types get their nesting level from their
        parent).  Checking ``not deeper than'' is a "<=" test on the levels.

        22.y   For each access parameter, the static depth passed depends on
        the actual, as follows:
         22.z  If the actual is an expression of a named access type,
               pass the static nesting level of that type.

         22.aa  If the actual is an allocator, pass the static nesting
               level of the caller, plus one.

         22.bb  If the actual is a reference to the Access attribute,
               pass the level of the view denoted by the prefix.

         22.cc  If the actual is a reference to the Unchecked_Access
               attribute, pass 0 (the library accessibility level).

         22.dd  If the actual is an access parameter, usually just pass
               along the level passed in.  However, if the static
               nesting level of the formal (access) parameter is greater
               than the static nesting level of the actual (access)
               parameter, the level to be passed is the minimum of the
               static nesting level of the access parameter and the
               actual level passed in.

        22.ee   For the Accessibility_Check associated with a type_conversion
        of an access parameter of a given subprogram to a named access type,
        if the target type is statically nested within the subprogram, do
        nothing; the check can't fail in this case.  Otherwise, check that
        the value passed in is <= the static nesting depth of the target
        type.  The other Accessibility_Checks are handled in a similar
        manner.

        22.ff   This method, using statically known values most of the time,
        is efficient, and, more importantly, avoids distributed overhead.

        22.gg   Discussion:  Examples of accessibility:

22.hh       package body Lib_Unit is
                type T is tagged ...;
                type A0 is access all T;
                Global: A0 := ...;
                procedure P(X: T) is
                    Y: aliased T;
                    type A1 is access all T;
                    Ptr0: A0 := Global; -- OK.
                    Ptr1: A1 := X'Access; -- OK.
                begin
                    Ptr1 := Y'Access; -- OK;
                    Ptr0 := A0(Ptr1); -- Illegal type conversion!
                    Ptr0 := X'Access; -- Illegal reference to Access attribute!
                    Ptr0 := Y'Access; -- Illegal reference to Access attribute!
                    Global := Ptr0; -- OK.
                end P;
            end Lib_Unit;

        22.ii   The above illegal statements are illegal because the
        accessibility level of X and Y are statically deeper than the
        accessibility level of A0.  In every possible execution of any
        program including this library unit, if P is called, the
        accessibility level of X will be (dynamically) deeper than that of
        A0.  Note that the accessibility levels of X and Y are the same.

        22.jj   Here's an example involving access parameters:

22.kk       procedure Main is
                type Level_1_Type is access all Integer;

22.ll           procedure P(X: access Integer) is
                    type Nested_Type is access all Integer;
                begin
                    ... Nested_Type(X) ... -- (1)
                    ... Level_1_Type(X) ... -- (2)
                end P;

22.mm           procedure Q(X: access Integer) is
                    procedure Nested(X: access Integer) is
                    begin
                        P(X);
                    end Nested;
                begin
                    Nested(X);
                end Q;

22.nn           procedure R is
                    Level_2: aliased Integer;
                begin
                    Q(Level_2'Access); -- (3)
                end R;

22.oo           Level_1: aliased Integer;
            begin
                Q(Level_1'Access); -- (4)
                R;
            end Main;

        22.pp   The run-time Accessibility_Check at (1) can never fail, and
        no code should be generated to check it.  The check at (2) will fail
        when called from (3), but not when called from (4).

        22.qq   Within a type_declaration, the rules are checked in an
        assume-the-worst manner.  For example:

22.rr       package P is
                type Int_Ptr is access all Integer;
                type Rec(D: access Integer) is limited private;
            private
                type Rec_Ptr is access all Rec;
                function F(X: Rec_Ptr) return Boolean;
                function G(X: access Rec) return Boolean;
                type Rec(D: access Integer) is
                    record
                        C1: Int_Ptr := Int_Ptr(D); -- Illegal!
                        C2: Rec_Ptr := Rec'Access; -- Illegal!
                        C3: Boolean := F(Rec'Access); -- Illegal!
                        C4: Boolean := G(Rec'Access);
                    end record;
            end P;

        22.ss   C1, C2, and C3 are all illegal, because one might declare an
        object of type Rec at a more deeply nested place than the declaration
        of the type.  C4 is legal, but the accessibility level of the object
        will be passed to function G, and constraint checks within G will
        prevent it from doing any evil deeds.

        22.tt   Note that we cannot defer the checks on C1, C2, and C3 until
        compile-time of the object creation, because that would cause
        violation of the privacy of private parts.  Furthermore, the problems
        might occur within a task or protected body, which the compiler can't
        see while compiling an object creation.

23   The following attribute is defined for a prefix X that denotes an
aliased view of an object:

24  X'Access
                X'Access yields an access value that designates the object
                denoted by X. The type of X'Access is an access-to-object
                type, as determined by the expected type.  The expected type
                shall be a general access type.  {Unchecked_Access attribute:
                see also Access attribute} X shall denote an aliased view of
                an object[, including possibly the current instance (see 8.6)
                of a limited type within its definition, or a formal
                parameter or generic formal object of a tagged type].
                {94-4978.a} The view denoted by the prefix X shall satisfy
                the following additional requirements, presuming the expected
                type for X'Access is the general access type A:

                   25  If A is an access-to-variable type, then the view
                       shall be a variable; [on the other hand, if A is
                       an access-to-constant type, the view may be
                       either a constant or a variable.]

 25.a   Discussion:  The current instance of a limited type is
        considered a variable.

                   26  The view shall not be a subcomponent that depends
                       on discriminants of a variable whose nominal
                       subtype is unconstrained, unless this subtype is
                       indefinite, or the variable is aliased.

 26.a   Change:  Fixed this rule to match the rule for renaming (see 8.5.1,
        ``Object Renaming Declarations'').

 26.b   Discussion:  This restriction is intended to be similar to the
        restriction on renaming discriminant-dependent subcomponents.

 26.c   Reason:  This prevents references to subcomponents that might
        disappear or move or change constraints after creating the
        reference.

 26.d   Implementation Note:  There was some thought to making this
        restriction more stringent, roughly:  "X shall not denote a
        subcomponent of a variable with discriminant-dependent
        subcomponents, if the nominal subtype of the variable is an
        unconstrained definite subtype."  This was because in some
        implementations, it is not just the discriminant-dependent
        subcomponents that might move as the result of an assignment
        that changed the discriminants of the enclosing object.
        However, it was decided not to make this change because a
        reasonable implementation strategy was identified to avoid such
        problems, as follows:

         26.e  Place non-discriminant-dependent components with any
               aliased parts at offsets preceding any discriminant-
               dependent components in a discriminated record type with
               defaulted discriminants.

         26.f  Preallocate the maximum space for unconstrained
               discriminated variables with aliased subcomponents,
               rather than allocating the initial size and moving them
               to a larger (heap-resident) place if they grow as the
               result of an assignment.

 26.g   Note that for objects of a by-reference type, it is not an error
        for a programmer to take advantage of the fact that such objects
        are passed by reference.  Therefore, the above approach is also
        necessary for discriminated record types with components of a
        by-reference type.

 26.h   To make the above strategy work, it is important that a
        component of a derived type is defined to be discriminant-
        dependent if it is inherited and the parent subtype constraint
        is defined in terms of a discriminant of the derived type (see
        3.7).

                   27  If the designated type of A is tagged, then the
                       type of the view shall be covered by the
                       designated type; if A's designated type is not
                       tagged, then the type of the view shall be the
                       same, and either A's designated subtype shall
                       statically match the nominal subtype of the view,
                       or the designated subtype shall be discriminated
                       and unconstrained; {statically matching
                       [required]}

 27.a   Implementation Note:  This ensures that the dope for an aliased
        array object can always be stored contiguous with it, but need
        not be if its nominal subtype is constrained.

                   28  The accessibility level of the view shall not be
                       statically deeper than that of the access type A.
                       {94-4715.a} In addition to the places where
                       Legality Rules normally apply (see 12.3), this
                       rule applies also in the private part of an
                       instance of a generic unit.  {accessibility rule
                       [Access attribute]} {generic contract issue
                       [partial]}

 28.a   Ramification:  In an instance body, a run-time check applies.

 28.b   If A is an anonymous access type, then the view can never have a
        deeper accessibility level than A, except when X'Access is used
        to initialize an access discriminant of an object created by an
        allocator.  The latter case is illegal if the accessibility
        level of X is statically deeper than that of the access type of
        the allocator; a run-time check is needed in the case where the
        initial value comes from an access parameter.  {94-4715.a}

                29   {Accessibility_Check [partial]} {check, language-defined
                (Accessibility_Check)} {Program_Error (raised by failure of
                run-time check)} A check is made that the accessibility level
                of X is not deeper than that of the access type A.
                {94-4715.a} If this check fails, Program_Error is raised.

        29.a   Ramification:  The check is needed for access parameters and
        in instance bodies.

        29.b   Implementation Note:  This check requires that some indication
        of lifetime is passed as an implicit parameter along with access
        parameters.  No such requirement applies to access discriminants,
        since the checks associated with them are all compile-time checks.

                30   {implicit subtype conversion [Access attribute]} If the
                nominal subtype of X does not statically match the designated
                subtype of A, a view conversion of X to the designated
                subtype is evaluated (which might raise Constraint_Error --
                see 4.6) and the value of X'Access designates that view.

31   The following attribute is defined for a prefix P that denotes a
subprogram:

32  P'Access
                P'Access yields an access value that designates the
                subprogram denoted by P. The type of P'Access is an
                access-to-subprogram type (S), as determined by the expected
                type.  {accessibility rule [Access attribute]} The
                accessibility level of P shall not be statically deeper than
                that of S.  {94-4715.a} {generic contract issue [partial]} In
                addition to the places where Legality Rules normally apply
                (see 12.3), this rule applies also in the private part of an
                instance of a generic unit.  The profile of P shall be
                subtype-conformant with the designated profile of S, and
                shall not be Intrinsic.  {94-4774.b} {subtype conformance
                (required)} If the subprogram denoted by P is declared within
                a generic body, S shall be declared within the generic body.
                {94-4692.a} {94-4702.a} {94-4706.a} {94-4708.a}

32.a    Discussion:  The part about generic bodies is worded in terms of the
        denoted subprogram, not the denoted view; this implies that renaming
        is invisible to this part of the rule.  This rule is partly to
        prevent contract model problems with respect to the accessibility
        rules, and partly to ease shared-generic-body implementations, in
        which a subprogram declared in an instance needs to have a different
        calling convention from other subprograms with the same profile.

32.b    Overload resolution ensures only that the profile is type-conformant.
        This rule specifies that subtype conformance is required (which also
        requires matching calling conventions).  P cannot denote an entry
        because access-to-subprogram types never have the entry calling
        convention.  P cannot denote an enumeration literal or an attribute
        function because these have intrinsic calling conventions.


     NOTES
33   (81) The Unchecked_Access attribute yields the same result as the Access
     attribute for objects, but has fewer restrictions (see 13.10).  There
     are other predefined operations that yield access values:  an allocator
     can be used to create an object, and return an access value that
     designates it (see 4.8); evaluating the literal null yields a null
     access value that designates no entity at all (see 4.2).

34   (82) {predefined operations [of an access type]} The predefined
     operations of an access type also include the assignment operation,
     qualification, and membership tests.  Explicit conversion is allowed
     between general access types with matching designated subtypes; explicit
     conversion is allowed between access-to-subprogram types with subtype
     conformant profiles (see 4.6).  {subtype conformance [partial]} Named
     access types have predefined equality operators; anonymous access types
     do not (see 4.5.2).

   34.a   Reason:  By not having equality operators for anonymous access
        types, we eliminate the need to specify exactly where the predefined
        operators for anonymous access types would be defined, as well as the
        need for an implementer to insert an implicit declaration for "=",
        etc. at the appropriate place in their symbol table.  Note that
        'Access and ".all" are defined, and ":=" is defined though useless
        since all instances are constant.  The literal null is also defined
        for the purposes of overload resolution, but is disallowed by a
        Legality Rule of this subclause.

35   (83) The object or subprogram designated by an access value can be named
     with a dereference, either an explicit_dereference or an implicit_
     dereference.  See 4.1.

36   (84) A call through the dereference of an access-to-subprogram value is
     never a dispatching call.

   36.a   Proof:  See 3.9.2.

37   (85) {downward closure} {closure (downward)} The accessibility rules
     imply that it is not possible to use the Access attribute to implement
     ``downward closures'' -- that is, to pass a more-nested subprogram as a
     parameter to a less-nested subprogram, as might be desired for example
     for an iterator abstraction.  Instead, downward closures can be
     implemented using generic formal subprograms (see 12.6).  Note that
     Unchecked_Access is not allowed for subprograms.

38   (86) Note that using an access-to-class-wide tagged type with a
     dispatching operation is a potentially more structured alternative to
     using an access-to-subprogram type.

39   (87) An implementation may consider two access-to-subprogram values to
     be unequal, even though they designate the same subprogram.  This might
     be because one points directly to the subprogram, while the other points
     to a special prologue that performs an Elaboration_Check and then jumps
     to the subprogram.  See 4.5.2.

   39.a   Ramification:  If equality of access-to-subprogram values is
        important to the logic of a program, a reference to the Access
        attribute of a subprogram should be evaluated only once and stored in
        a global constant for subsequent use and equality comparison.


                                  Examples

40   Example of use of the Access attribute:

41  Martha : Person_Name := new Person(F);       -- see 3.10.1
    Cars   : array (1..2) of aliased Car;
       ...
    Martha.Vehicle := Cars(1)'Access;
    George.Vehicle := Cars(2)'Access;


                            Extensions to Ada 83

        41.a   {extensions to Ada 83} We no longer make things like 'Last and
        ".component" (basic) operations of an access type that need to be
        "declared" somewhere.  Instead, implicit dereference in a prefix
        takes care of them all.  This means that there should never be a case
        when X.all'Last is legal while X'Last is not.  See AI-00154.



3.11 Declarative Parts

1   [A declarative_part contains declarative_items (possibly none).]


                                   Syntax

2   declarative_part ::= {declarative_item}

3   declarative_item ::=
        basic_declarative_item | body

4   basic_declarative_item ::=
        basic_declaration | representation_clause | use_clause

5   body ::= proper_body | body_stub

6   proper_body ::=
        subprogram_body | package_body | task_body | protected_body


                              Dynamic Semantics

7   {elaboration [declarative_part]} The elaboration of a declarative_part
consists of the elaboration of the declarative_items, if any, in the order in
which they are given in the declarative_part.

8   {elaborated} An elaborable construct is in the elaborated state after the
normal completion of its elaboration.  Prior to that, it is not yet
elaborated.
        8.a   Ramification:  The elaborated state is only important for
        bodies; certain uses of a body raise an exception if the body is not
        yet elaborated.

        8.b   Note that "prior" implies before the start of elaboration, as
        well as during elaboration.

        8.c   The use of the term "normal completion" implies that if the
        elaboration propagates an exception or is aborted, the declaration is
        not elaborated.  RM83 missed the aborted case.

9   {Elaboration_Check [partial]} {check, language-defined (Elaboration_
Check)} For a construct that attempts to use a body, a check (Elaboration_
Check) is performed, as follows:

   10  For a call to a (non-protected) subprogram that has an explicit
       body, a check is made that the subprogram_body is already
       elaborated.  This check and the evaluations of any actual
       parameters of the call are done in an arbitrary order.

 10.a   Discussion:  AI-00180 specifies that there is no elaboration
        check for a subprogram defined by a pragma Interface (or
        equivalently, pragma Import).  AI-00430 specifies that there is
        no elaboration check for an enumeration literal.  AI-00406
        specifies that the evaluation of parameters and the elaboration
        check occur in an arbitrary order.  AI-00406 applies to generic
        instantiation as well (see below).

   11  For a call to a protected operation of a protected type (that has
       a body -- no check is performed if a pragma Import applies to the
       protected type), a check is made that the protected_body is
       already elaborated.  This check and the evaluations of any actual
       parameters of the call are done in an arbitrary order.

 11.a   Discussion:  A protected type has only one elaboration ``bit,''
        rather than one for each operation, because one call may result
        in evaluating the barriers of other entries, and because there
        are no elaborable declarations between the bodies of the
        operations.  In fact, the elaboration of a protected_body does
        not elaborate the enclosed bodies, since they are not considered
        independently elaborable.

 11.b   Note that there is no elaboration check when calling a task
        entry.  Task entry calls are permitted even before the
        associated task_body has been seen.  Such calls are simply
        queued until the task is activated and reaches a corresponding
        accept_statement.  We considered a similar rule for protected
        entries -- simply queuing all calls until the protected_body was
        seen, but felt it was not worth the possible implementation
        overhead, particularly given that there might be multiple
        instances of the protected type.

   12  For the activation of a task, a check is made by the activator
       that the task_body is already elaborated.  If two or more tasks
       are being activated together (see 9.2), as the result of the
       elaboration of a declarative_part or the initialization for the
       object created by an allocator, this check is done for all of
       them before activating any of them.

        12.a   Reason:  As specified by AI-00149, the check is done by
        the activator, rather than by the task itself.  If it were done
        by the task itself, it would be turned into a Tasking_Error in
        the activator, and the other tasks would still be activated.

   13  For the instantiation of a generic unit that has a body, a check
       is made that this body is already elaborated.  This check and the
       evaluation of any explicit_generic_actual_parameters of the
       instantiation are done in an arbitrary order.

14   {Program_Error (raised by failure of run-time check)} The exception
Program_Error is raised if any of these checks fails.


                            Extensions to Ada 83

        14.a   {extensions to Ada 83} The syntax for declarative_part is
        modified to remove the ordering restrictions of Ada 83; that is, the
        distinction between basic_declarative_items and later_declarative_
        items within declarative_parts is removed.  This means that things
        like use_clauses and variable_declarations can be freely intermixed
        with things like bodies.

        14.b   The syntax rule for proper_body now allows a protected_body,
        and the rules for elaboration checks now cover calls on protected
        operations.

                         Wording Changes From Ada 83

        14.c   The syntax rule for later_declarative_item is removed; the
        syntax rule for declarative_item is new.

        14.d   RM83 defines ``elaborated'' and ``not yet elaborated'' for
        declarative_items here, and for other things in 3.1, ``Declara-
        tions''.  That's no longer necessary, since these terms are fully
        defined in 3.1.

        14.e   In RM83, all uses of declarative_part are optional (except for
        the one in block_statement with a declare) which is sort of strange,
        since a declarative_part can be empty, according to the syntax.  That
        is, declarative_parts are sort of ``doubly optional''.  In Ada 9X,
        these declarative_parts are always required (but can still be empty).
        To simplify description, we go further and say (see 5.6, ``Block
        Statements'') that a block_statement without an explicit declarative_
        part is equivalent to one with an empty one.



3.11.1 Completions of Declarations

1   Declarations sometimes come in two parts.  {requires a completion} A
declaration that requires a second part is said to require completion.
{completion (compile-time concept)} The second part is called the completion
of the declaration (and of the entity declared), and is either another
declaration, a body, or a pragma.

        1.a   Discussion:  Throughout the RM9X, there are rules about
        completions that define the following:

          1.b  Which declarations require a corresponding completion.

          1.c  Which constructs can only serve as the completion of a
               declaration.

          1.d  Where the completion of a declaration is allowed to be.

          1.e  What kinds of completions are allowed to correspond to
               each kind of declaration that allows one.

        1.f   Don't confuse this compile-time concept with the run-time
        concept of completion defined in 7.6.1.

        1.g   Note that the declaration of a private type (if limited) can be
        completed with the declaration of a task type, which is then
        completed with a body.  Thus, a declaration can actually come in
        three parts.


                            Name Resolution Rules

2   A construct that can be a completion is interpreted as the completion of
a prior declaration only if:

    3  The declaration and the completion occur immediately within the
       same declarative region;

    4  The defining name or defining_program_unit_name in the completion
       is the same as in the declaration, or in the case of a pragma,
       the pragma applies to the declaration;

    5  If the declaration is overloadable, then the completion either
       has a type-conformant profile, or is a pragma.  {type conformance
       (required)}


                               Legality Rules

6   An implicit declaration shall not have a completion.  {requires a
completion [distributed]} For any explicit declaration that is specified to
require completion, there shall be a corresponding explicit completion.

        6.a   Discussion:  The implicit declarations of predefined operators
        are not allowed to have a completion.  Enumeration literals, although
        they are subprograms, are not allowed to have a corresponding
        subprogram_body.  That's because the completion rules are described
        in terms of constructs (subprogram_declarations) and not entities
        (subprograms).  When a completion is required, it has to be explicit;
        the implicit null package_body that Section 7 talks about cannot
        serve as the completion of a package_declaration if a completion is
        required.

7   At most one completion is allowed for a given declaration.  Additional
requirements on completions appear where each kind of completion is defined.

        7.a   Ramification:  A subunit is not a completion; the stub is.

        7.b   If the completion of a declaration is also a declaration, then
        that declaration might have a completion, too.  For example, a
        limited private type can be completed with a task type, which can
        then be completed with a task body.  This is not a violation of the
        ``at most one completion'' rule.

8   {completely defined} A type is completely defined at a place that is
after its full type definition (if it has one) and after all of its
subcomponent types are completely defined.  A type shall be completely
defined before it is frozen (see 13.14 and 7.3).

        8.a   Change:  Rule moved here from 13.14, ``Freezing Rules'', as per
        WG9 resolution.

        8.b   Reason:  Index types are always completely defined -- no need
        to mention them.  There is no way for a completely defined type to
        depend on the value of a (still) deferred constant.


     NOTES
9    (88) Completions are in principle allowed for any kind of explicit
     declaration.  However, for some kinds of declaration, the only allowed
     completion is a pragma Import, and implementations are not required to
     support pragma Import for every kind of entity.
   9.a   Discussion:  In fact, we expect that implementations will not
        support pragma Import of things like types -- it's hard to even
        define the semantics of what it would mean.  Therefore, in practice,
        not every explicit declaration can have a completion.  In any case,
        if an implementation chooses to support pragma Import for, say,
        types, it can place whatever restrictions on the feature it wants to.
        For example, it might want the pragma to be a freezing point for the
        type.

10   (89) There are rules that prevent premature uses of declarations that
     have a corresponding completion.  The Elaboration_Checks of 3.11 prevent
     such uses at run time for subprograms, protected operations, tasks, and
     generic units.  The rules of 13.14, ``Freezing Rules'' prevent, at
     compile time, premature uses of other entities such as private types and
     deferred constants.


                         Wording Changes From Ada 83

        10.a   This subclause is new.  It is intended to cover all kinds of
        completions of declarations, be they a body for a spec, a full type
        for an incomplete or private type, a full constant declaration for a
        deferred constant declaration, or a pragma Import for any kind of
        entity.



                      Section 4: Names and Expressions


1   [The rules applicable to the different forms of name and expression, and
to their evaluation, are given in this section.]



4.1 Names

1   [Names can denote declared entities, whether declared explicitly or
implicitly (see 3.1).  Names can also denote objects or subprograms
designated by access values; the results of type_conversions or function_
calls; subcomponents and slices of objects and values; protected subprograms,
single entries, entry families, and entries in families of entries.  Finally,
names can denote attributes of any of the foregoing.]


                                   Syntax

2   name ::=
         direct_name                | explicit_dereference
       | indexed_component          | slice
       | selected_component         | attribute_reference
       | type_conversion            | function_call
       | character_literal

3   direct_name ::= identifier | operator_symbol

        3.a   Discussion:  character_literal is no longer a direct_name.
        character_literals are usable even when the corresponding
        enumeration_type_declaration is not visible.  See 4.2.

4   prefix ::= name | implicit_dereference

5   explicit_dereference ::= name.all

6   implicit_dereference ::= name


7   [Certain forms of name (indexed_components, selected_components, slices,
and attributes) include a prefix that is either itself a name that denotes
some related entity, or an implicit_dereference of an access value that
designates some related entity.]


                            Name Resolution Rules

8   {dereference} {expected type [dereference name]} The name in a
dereference (either an implicit_dereference or an explicit_dereference) is
expected to be of any access type.


                              Static Semantics

9   {nominal subtype [associated with a dereference]} If the type of the name
in a dereference is some access-to-object type T, then the dereference
denotes a view of an object, the nominal subtype of the view being the
designated subtype of T.

        9.a   Ramification:  If the value of the name is the result of an
        access type conversion, the dereference denotes a view created as
        part of the conversion.  The nominal subtype of the view is not
        necessarily the same as that used to create the designated object.
        See 4.6.

        9.b   To be honest:  {nominal subtype [of a name]} We sometimes refer
        to the nominal subtype of a particular kind of name rather than the
        nominal subtype of the view denoted by the name (presuming the name
        denotes a view of an object).  These two uses of nominal subtype are
        intended to mean the same thing.

10   {profile [associated with a dereference]} If the type of the name in a
dereference is some access-to-subprogram type S, then the dereference denotes
a view of a subprogram, the profile of the view being the designated profile
of S.

        10.a   Ramification:  This means that the formal parameter names and
        default expressions to be used in a call whose name or prefix is a
        dereference are those of the designated profile, which need not be
        the same as those of the subprogram designated by the access value,
        since 'Access requires only subtype conformance, not full
        conformance.


                              Dynamic Semantics

11   {evaluation [name]} The evaluation of a name determines the entity
denoted by the name.  This evaluation has no other effect for a name that is
a direct_name or a character_literal.

12   {evaluation [name that has a prefix]} [The evaluation of a name that has
a prefix includes the evaluation of the prefix.]  {evaluation [prefix]} The
evaluation of a prefix consists of the evaluation of the name or the
implicit_dereference.  The prefix denotes the entity denoted by the name or
the implicit_dereference.

13   {evaluation [dereference]} The evaluation of a dereference consists of
the evaluation of the name and the determination of the object or subprogram
that is designated by the value of the name.  {Access_Check [partial]}
{check, language-defined (Access_Check)} A check is made that the value of
the name is not the null access value.  {Constraint_Error (raised by failure
of run-time check)} Constraint_Error is raised if this check fails.  The
dereference denotes the object or subprogram designated by the value of the
name.


                                  Examples

14   Examples of direct names:

15
    Pi             -- the direct name of a number                  (see 3.3.2)
    Limit          -- the direct name of a constant                (see 3.3.1)
    Count          -- the direct name of a scalar variable         (see 3.3.1)
    Board          -- the direct name of an array variable         (see 3.6.1)
    Matrix         -- the direct name of a type                    (see 3.6)
    Random         -- the direct name of a function                (see 6.1)
    Error          -- the direct name of an exception              (see 11.1)

16   Examples of dereferences:

17
    Next_Car.all         --  explicit dereference denoting the object designate\
d by
                         --  the access variable Next_Car (see 3.10.1)
    Next_Car.Owner       --  selected component with implicit dereference;
                         --  same as Next_Car.all.Owner


                            Extensions to Ada 83

        17.a   {extensions to Ada 83} Type conversions and function calls are
        now considered names that denote the result of the operation.  In the
        case of a type conversion used as an actual parameter or that is of a
        tagged type, the type conversion is considered a variable if the
        operand is a variable.  This simplifies the description of
        "parameters of the form of a type conversion" as well as better
        supporting an important OOP paradigm that requires the combination of
        a conversion from a class-wide type to some specific type followed
        immediately by component selection.  Function calls are considered
        names so that a type conversion of a function call and the function
        call itself are treated equivalently in the grammar.  A function call
        is considered the name of a constant, and can be used anywhere such a
        name is permitted.  See 6.5.

        17.b   Type conversions of a tagged type are permitted anywhere their
        operand is permitted.  That is, if the operand is a variable, then
        the type conversion can appear on the left-hand side of an
        assignment_statement.  If the operand is an object, then the type
        conversion can appear in an object renaming or as a prefix.  See 4.6.

                         Wording Changes From Ada 83

        17.c   Everything of the general syntactic form name(...) is now
        syntactically a name.  In any realistic parser, this would be a
        necessity since distinguishing among the various name(...) constructs
        inevitably requires name resolution.  In cases where the construct
        yields a value rather than an object, the name denotes the value
        rather than an object.  Names already denote values in Ada 83 with
        named numbers, components of the result of a function call, etc.
        This is partly just a wording change, and partly an extension of
        functionality (see Extensions heading above).

        17.d   The syntax rule for direct_name is new.  It is used in places
        where direct visibility is required.  It's kind of like Ada 83's
        simple_name, but simple_name applied to both direct visibility and
        visibility by selection, and furthermore, it didn't work right for
        operator_symbols.  The syntax rule for simple_name is removed, since
        its use is covered by a combination of direct_name and selector_name.
        The syntactic categories direct_name and selector_name are similar;
        it's mainly the visibility rules that distinguish the two.  The
        introduction of direct_name requires the insertion of one new
        explicit textual rule: to forbid statement_identifiers from being
        operator_symbols.  This is the only case where the explicit rule is
        needed, because this is the only case where the declaration of the
        entity is implicit.  For example, there is no need to syntactically
        forbid (say) ``X: "Rem";'', because it is impossible to declare a
        type whose name is an operator_symbol in the first place.

        17.e   The syntax rules for explicit_dereference and implicit_
        dereference are new; this makes other rules simpler, since
        dereferencing an access value has substantially different semantics
        from selected_components.  We also use name instead of prefix in the
        explicit_dereference rule since that seems clearer.  Note that these
        rules rely on the fact that function calls are now names, so we don't
        need to use prefix to allow functions calls in front of .all.

        17.f   Discussion:  Actually, it would be reasonable to allow any
        primary in front of .all, since only the value is needed, but that
        would be a bit radical.

        17.g   We no longer use the term appropriate for a type since we now
        describe the semantics of a prefix in terms of implicit dereference.



4.1.1 Indexed Components

1   [An indexed_component denotes either a component of an array or an entry
in a family of entries.  {array indexing: see indexed_component} ]


                                   Syntax

2   indexed_component ::= prefix(expression {, expression})


                            Name Resolution Rules

3   The prefix of an indexed_component with a given number of expressions
shall resolve to denote an array (after any implicit dereference) with the
corresponding number of index positions, or shall resolve to denote an entry
family of a task or protected object (in which case there shall be only one
expression).

4   {expected type [indexed_component expression]} The expected type for each
expression is the corresponding index type.


                              Static Semantics

5   When the prefix denotes an array, the indexed_component denotes the
component of the array with the specified index value(s).  {nominal subtype
[associated with an indexed_component]} The nominal subtype of the indexed_
component is the component subtype of the array type.

        5.a   Ramification:  In the case of an array whose components are
        aliased, and of an unconstrained discriminated subtype, the
        components are constrained even though their nominal subtype is
        unconstrained.  (This is because all aliased discriminated objects
        are constrained.  See 3.10.2.)  In all other cases, an array
        component is constrained if and only if its nominal subtype is
        constrained.

6   When the prefix denotes an entry family, the indexed_component denotes
the individual entry of the entry family with the specified index value.


                              Dynamic Semantics

7   {evaluation [indexed_component]} For the evaluation of an indexed_
component, the prefix and the expressions are evaluated in an arbitrary
order.  The value of each expression is converted to the corresponding index
type.  {implicit subtype conversion [array index]} {Index_Check [partial]}
{check, language-defined (Index_Check)} A check is made that each index value
belongs to the corresponding index range of the array or entry family denoted
by the prefix.  {Constraint_Error (raised by failure of run-time check)}
Constraint_Error is raised if this check fails.


                                  Examples

8   Examples of indexed components:

9
     My_Schedule(Sat)     --  a component of a one-dimensional array  (see 3.6.\
1)
     Page(10)             --  a component of a one-dimensional array  (see 3.6)
     Board(M, J + 1)      --  a component of a two-dimensional array  (see 3.6.\
1)
     Page(10)(20)         --  a component of a component              (see 3.6)
     Request(Medium)      --  an entry in a family of entries         (see 9.1)
     Next_Frame(L)(M, N)  --  a component of a function call          (see 6.1)


     NOTES
10   (1) Notes on the examples:  Distinct notations are used for components
     of multidimensional arrays (such as Board) and arrays of arrays (such as
     Page).  The components of an array of arrays are arrays and can
     therefore be indexed.  Thus Page(10)(20) denotes the 20th component of
     Page(10).  In the last example Next_Frame(L) is a function call
     returning an access value that designates a two-dimensional array.



4.1.2 Slices

1   [{array slice} A slice denotes a one-dimensional array formed by a
sequence of consecutive components of a one-dimensional array.  A slice of a
variable is a variable; a slice of a constant is a constant;] a slice of a
value is a value.


                                   Syntax

2   slice ::= prefix(discrete_range)


                            Name Resolution Rules

3   The prefix of a slice shall resolve to denote a one-dimensional array
(after any implicit dereference).

4   {expected type [slice discrete_range]} The expected type for the
discrete_range of a slice is the index type of the array type.


                              Static Semantics

5   A slice denotes a one-dimensional array formed by the sequence of
consecutive components of the array denoted by the prefix, corresponding to
the range of values of the index given by the discrete_range.

6   The type of the slice is that of the prefix.  Its bounds are those
defined by the discrete_range.


                              Dynamic Semantics

7   {evaluation [slice]} For the evaluation of a slice, the prefix and the
discrete_range are evaluated in an arbitrary order.  {Index_Check [partial]}
{check, language-defined (Index_Check)} {null slice} If the slice is not a
null slice (a slice where the discrete_range is a null range), then a check
is made that the bounds of the discrete_range belong to the index range of
the array denoted by the prefix.  {Constraint_Error (raised by failure of
run-time check)} Constraint_Error is raised if this check fails.


     NOTES
8    (2) A slice is not permitted as the prefix of an Access attribute_
     reference, even if the components or the array as a whole are aliased.
     See 3.10.2.

   8.a   Proof:  Slices are not aliased, by 3.10, ``Access Types''.

   8.b   Reason:  This is to ease implementation of general-access-to-array.
        If slices were aliased, implementations would need to store array
        dope with the access values, which is not always desirable given
        access-to-incomplete types completed in a package body.

9    (3) For a one-dimensional array A, the slice A(N .. N) denotes an array
     that has only one component; its type is the type of A. On the other
     hand, A(N) denotes a component of the array A and has the corresponding
     component type.


                                  Examples

10   Examples of slices:

11
      Stars(1 .. 15)        --  a slice of 15 characters                  (see \
3.6.3)
      Page(10 .. 10 + Size) --  a slice of 1 + Size components            (see \
3.6)
      Page(L)(A .. B)       --  a slice of the array Page(L)              (see \
3.6)
      Stars(1 .. 0)         --  a null slice                              (see \
3.6.3)
      My_Schedule(Weekday)  --  bounds given by subtype                   (see \
3.6.1 and 3.5.1)
      Stars(5 .. 15)(K)     --  same as Stars(K)                          (see \
3.6.3)
                            --  provided that K is in 5 .. 15



4.1.3 Selected Components

1   [Selected_components are used to denote components (including
discriminants), entries, entry families, and protected subprograms; they are
also used as expanded names as described below.  {dot selection: see
selected_component}]


                                   Syntax

2   selected_component ::= prefix . selector_name

3   selector_name ::= identifier | character_literal | operator_symbol


                            Name Resolution Rules

4   {expanded name} A selected_component is called an expanded name if,
according to the visibility rules, at least one possible interpretation of
its prefix denotes a package or an enclosing named construct (directly, not
through a subprogram_renaming_declaration or generic_renaming_declaration).

        4.a   Discussion:  See AI-00187.

5   A selected_component that is not an expanded name shall resolve to denote
one of the following:

        5.a   Ramification:  If the prefix of a selected_component denotes an
        enclosing named construct, then the selected_component is interpreted
        only as an expanded name, even if the named construct is a function
        that could be called without parameters.

    6  A component [(including a discriminant)]:

       7   The prefix shall resolve to denote an object or value of some
       non-array composite type (after any implicit dereference).
       {94-4493.c} The selector_name shall resolve to denote a
       discriminant_specification of the type, or, unless the type is a
       protected type, a component_declaration of the type.  The
       selected_component denotes the corresponding component of the
       object or value.

        7.a   Reason:  The components of a protected object cannot be
        named except by an expanded name, even from within the
        corresponding protected body.  The protected body may not
        reference the the private components of some arbitrary object of
        the protected type; the protected body may reference components
        of the current instance only (by an expanded name or a direct_
        name).

        7.b   Ramification:  Only the discriminants and components
        visible at the place of the selected_component can be selected,
        since a selector_name can only denote declarations that are
        visible (see 8.3).

    8  A single entry, an entry family, or a protected subprogram:

       9   The prefix shall resolve to denote an object or value of some
       task or protected type (after any implicit dereference).  The
       selector_name shall resolve to denote an entry_declaration or
       subprogram_declaration occurring (implicitly or explicitly)
       within the visible part of that type.  The selected_component
       denotes the corresponding entry, entry family, or protected
       subprogram.

        9.a   Reason:  This explicitly says ``visible part'' because
        even though the body has visibility on the private part, it
        cannot call the private operations of some arbitrary object of
        the task or protected type, only those of the current instance
        (and expanded name notation has to be used for that).

10   An expanded name shall resolve to denote a declaration that occurs
immediately within a named declarative region, as follows:

   11  The prefix shall resolve to denote either a package [(including
       the current instance of a generic package, or a rename of a
       package)], or an enclosing named construct.

   12  The selector_name shall resolve to denote a declaration that
       occurs immediately within the declarative region of the package
       or enclosing construct [(the declaration shall be visible at the
       place of the expanded name -- see 8.3)].  The expanded name
       denotes that declaration.

 12.a   Ramification:  Hence, a library unit or subunit can use an
        expanded name to refer to the declarations within the private
        part of its parent unit, as well as to other children that have
        been mentioned in with_clauses.

   13  If the prefix does not denote a package, then it shall be a
       direct_name or an expanded name, and it shall resolve to denote a
       program unit (other than a package), the current instance of a
       type, a block_statement, a loop_statement, or an accept_statement
       (in the case of an accept_statement or entry_body, no family
       index is allowed); the expanded name shall occur within the
       declarative region of this construct.  Further, if this construct
       is a callable construct and the prefix denotes more than one such
       enclosing callable construct, then the expanded name is
       ambiguous, independently of the selector_name.


                              Dynamic Semantics

14   {evaluation [selected_component]} The evaluation of a selected_component
includes the evaluation of the prefix.

15   {Discriminant_Check [partial]} {check, language-defined (Discriminant_
Check)} For a selected_component that denotes a component of a variant, a
check is made that the values of the discriminants are such that the value or
object denoted by the prefix has this component.  {Constraint_Error (raised
by failure of run-time check)} {Constraint_Error (raised by failure of
run-time check)} The exception Constraint_Error is raised if this check
fails.


                                  Examples

16   Examples of selected components:

17
      Tomorrow.Month     --  a record component                             (se\
e 3.8)
      Next_Car.Owner     --  a record component                             (se\
e 3.10.1)
      Next_Car.Owner.Age --  a record component                             (se\
e 3.10.1)
                         --  the previous two lines involve implicit dereferenc\
es
      Writer.Unit        --  a record component (a discriminant)            (se\
e 3.8.1)
      Min_Cell(H).Value  --  a record component of the result               (se\
e 6.1)
                         --  of the function call Min_Cell(H)
      Control.Seize      --  an entry of a protected object                 (se\
e 9.4)
      Pool(K).Write      --  an entry of the task Pool(K)                   (se\
e 9.4)

18   Examples of expanded names:

19
      Key_Manager."<"      --  an operator of the visible part of a package (se\
e 7.3.1)
      Dot_Product.Sum      --  a variable declared in a function body       (se\
e 6.1)
      Buffer.Pool          --  a variable declared in a protected unit      (se\
e 9.11)
      Buffer.Read          --  an entry of a protected unit                 (se\
e 9.11)
      Swap.Temp            --  a variable declared in a block statement     (se\
e 5.6)
      Standard.Boolean     --  the name of a predefined type                (se\
e A.1)


                            Extensions to Ada 83

        19.a   {extensions to Ada 83} We now allow an expanded name to use a
        prefix that denotes a rename of a package, even if the selector is
        for an entity local to the body or private part of the package, so
        long as the entity is visible at the place of the reference.  This
        eliminates a preexisting anomaly where references in a package body
        may refer to declarations of its visible part but not those of its
        private part or body when the prefix is a rename of the package.

                         Wording Changes From Ada 83

        19.b   The syntax rule for selector_name is new.  It is used in
        places where visibility, but not necessarily direct visibility, is
        required.  See 4.1, ``Names'' for more information.

        19.c   The description of dereferencing an access type has been moved
        to 4.1, ``Names''; name.all is no longer considered a selected_
        component.

        19.d   The rules have been restated to be consistent with our new
        terminology, to accommodate class-wide types, etc.



4.1.4 Attributes

1   {attribute} [An attribute is a characteristic of an entity that can be
queried via an attribute_reference or a range_attribute_reference.]


                                   Syntax

2   attribute_reference ::= prefix'attribute_designator

3   attribute_designator ::=
        identifier[(static_expression)]
      | Access | Delta | Digits

4   range_attribute_reference ::= prefix'range_attribute_designator

5   range_attribute_designator ::= Range[(static_expression)]


                            Name Resolution Rules

6   In an attribute_reference, if the attribute_designator is for an
attribute defined for (at least some) objects of an access type, then the
prefix is never interpreted as an implicit_dereference; otherwise (and for
all range_attribute_references), if the type of the name within the prefix is
of an access type, the prefix is interpreted as an implicit_dereference.
Similarly, if the attribute_designator is for an attribute defined for (at
least some) functions, then the prefix is never interpreted as a
parameterless function_call; otherwise (and for all range_attribute_
references), if the prefix consists of a name that denotes a function, it is
interpreted as a parameterless function_call.

        6.a   Discussion:  The first part of this rule is essentially a
        "preference" against implicit dereference, so that it is possible to
        ask for, say, 'Size of an access object, without automatically
        getting the size of the object designated by the access object.  This
        rule applies to 'Access, 'Unchecked_Access, 'Size, and 'Address, and
        any other attributes that are defined for at least some access
        objects.

        6.b   The second part of this rule implies that, for a parameterless
        function F, F'Address is the address of F, whereas F'Size is the size
        of the anonymous constant returned by F.

        6.c   We normally talk in terms of expected type or profile for name
        resolution rules, but we don't do this for attributes because certain
        attributes are legal independent of the type or the profile of the
        prefix.

7   {expected type [attribute_designator expression]} {expected type [range_
attribute_designator expression]} The expression, if any, in an attribute_
designator or range_attribute_designator is expected to be of any integer
type.
                               Legality Rules

8   The expression, if any, in an attribute_designator or range_attribute_
designator shall be static.


                              Static Semantics

9   An attribute_reference denotes a value, an object, a subprogram, or some
other kind of program entity.

        9.a   Ramification:  The attributes defined by the language are
        summarized in Annex K. Implementations can define additional
        attributes.

10   [A range_attribute_reference X'Range(N) is equivalent to the range
X'First(N) ..  X'Last(N), except that the prefix is only evaluated once.
Similarly, X'Range is equivalent to X'First .. X'Last, except that the prefix
is only evaluated once.]


                              Dynamic Semantics

11   {evaluation [attribute_reference]} {evaluation [range_attribute_
reference]} The evaluation of an attribute_reference (or range_attribute_
reference) consists of the evaluation of the prefix.


                         Implementation Permissions

12   An implementation may provide implementation-defined attributes; the
identifier for an implementation-defined attribute shall differ from those of
the language-defined attributes.

        12.a   Implementation defined:  Implementation-defined attributes.

        12.b   Ramification:  They cannot be reserved words because reserved
        words are not legal identifiers.

        12.c   The semantics of implementation-defined attributes, and any
        associated rules, are, of course, implementation defined.  For
        example, the implementation defines whether a given implementation-
        defined attribute can be used in a static expression.  {94-4539.b}


     NOTES
13   (4) Attributes are defined throughout this International Standard, and
     are summarized in Annex K.

14   (5) In general, the name in a prefix of an attribute_reference (or a
     range_attribute_reference) has to be resolved without using any context.
     However, in the case of the Access attribute, the expected type for the
     prefix has to be a single access type, and if it is an
     access-to-subprogram type (see 3.10.2) then the resolution of the name
     can use the fact that the profile of the callable entity denoted by the
     prefix has to be type conformant with the designated profile of the
     access type.  {type conformance (required)}

   14.a   Proof:  In the general case, there is no ``expected type'' for the
        prefix of an attribute_reference.  In the special case of 'Access,
        there is an ``expected profile'' for the prefix.

   14.b   Reason:  'Access is a special case, because without it, it would be
        very difficult to take 'Access of an overloaded subprogram.


                                  Examples

15   Examples of attributes:

16
    Color'First        -- minimum value of the enumeration type Color   (see 3.\
5.1)
    Rainbow'Base'First -- same as Color'First                           (see 3.\
5.1)
    Real'Digits        -- precision of the type Real                    (see 3.\
5.7)
    Board'Last(2)      -- upper bound of the second dimension of Board  (see 3.\
6.1)
    Board'Range(1)     -- index range of the first dimension of Board   (see 3.\
6.1)
    Pool(K)'Terminated -- True if task Pool(K) is terminated            (see 9.\
1)
    Date'Size          -- number of bits for records of type Date       (see 3.\
8)
    Message'Address    -- address of the record variable Message        (see 3.\
7.1)


                            Extensions to Ada 83

        16.a   {extensions to Ada 83} We now uniformly treat X'Range as
        X'First..X'Last, allowing its use with scalar subtypes.

        16.b   We allow any integer type in the static_expression of an
        attribute designator, not just a value of universal_integer.  The
        preference rules ensure upward compatibility.

                         Wording Changes From Ada 83

        16.c   We use the syntactic category attribute_reference rather than
        simply "attribute" to avoid confusing the name of something with the
        thing itself.

        16.d   The syntax rule for attribute_reference now uses identifier
        instead of simple_name, because attribute identifiers are not
        required to follow the normal visibility rules.

        16.e   We now separate attribute_reference from range_attribute_
        reference, and enumerate the reserved words that are legal attribute
        or range attribute designators.  We do this because identifier no
        longer includes reserved words.

        16.f   The Ada 9X name resolution rules are a bit more explicit than
        in Ada 83.  The Ada 83 rule said that the "meaning of the prefix of
        an attribute must be determinable independently of the attribute
        designator and independently of the fact that it is the prefix of an
        attribute."  That isn't quite right since the meaning even in Ada 83
        embodies whether or not the prefix is interpreted as a parameterless
        function call, and in Ada 9X, it also embodies whether or not the
        prefix is interpreted as an implicit_dereference.  So the attribute
        designator does make a difference -- just not much.

        16.g   Note however that if the attribute designator is Access, it
        makes a big difference in the interpretation of the prefix (see
        3.10.2).



4.2 Literals

1   [{literal} A literal represents a value literally, that is, by means of
notation suited to its kind.]  A literal is either a numeric_literal, a
character_literal, the literal null, or a string_literal.  {constant: see
also literal}

        1.a   Discussion:  An enumeration literal that is an identifier
        rather than a character_literal is not considered a literal in the
        above sense, because it involves no special notation ``suited to its
        kind.''  It might more properly be called an enumeration_identifier,
        except for historical reasons.


                            Name Resolution Rules

2   {expected type [null literal]} The expected type for a literal null shall
be a single access type.

        2.a   Discussion:  This new wording ("expected type ... shall be a
        single ... type") replaces the old "shall be determinable" stuff.  It
        reflects an attempt to simplify and unify the description of the
        rules for resolving aggregates, literals, type conversions, etc.  See
        8.6, ``The Context of Overload Resolution'' for the details.

3   {expected type [character_literal]} {expected profile [character_
literal]} For a name that consists of a character_literal, either its
expected type shall be a single character type, in which case it is
interpreted as a parameterless function_call that yields the corresponding
value of the character type, or its expected profile shall correspond to a
parameterless function with a character result type, in which case it is
interpreted as the name of the corresponding parameterless function declared
as part of the character type's definition (see 3.5.1).  In either case, the
character_literal denotes the enumeration_literal_specification.

        3.a   Discussion:  See 4.1.3 for the resolution rules for a selector_
        name that is a character_literal.

4   {expected type [string_literal]} The expected type for a primary that is
a string_literal shall be a single string type.


                               Legality Rules

5   A character_literal that is a name shall correspond to a defining_
character_literal of the expected type, or of the result type of the expected
profile.

6   For each character of a string_literal with a given expected string type,
there shall be a corresponding defining_character_literal of the component
type of the expected string type.

7   A literal null shall not be of an anonymous access type[, since such
types do not have a null value (see 3.10)].

        7.a   Reason:  This is a legality rule rather than an overloading
        rule, to simplify implementations.


                              Static Semantics

8   An integer literal is of type universal_integer.  A real literal is of
type universal_real.


                              Dynamic Semantics

9   {evaluation [numeric literal]} {evaluation [null literal]} {null access
value} {null pointer: see null access value} The evaluation of a numeric
literal, or the literal null, yields the represented value.

10   {evaluation [string_literal]} The evaluation of a string_literal that is
a primary yields an array value containing the value of each character of the
sequence of characters of the string_literal, as defined in 2.6.  The bounds
of this array value are determined according to the rules for positional_
array_aggregates (see 4.3.3), except that for a null string literal, the
upper bound is the predecessor of the lower bound.

11   {Range_Check [partial]} {check, language-defined (Range_Check)} For the
evaluation of a string_literal of type T, a check is made that the value of
each character of the string_literal belongs to the component subtype of T.
For the evaluation of a null string literal, a check is made that its lower
bound is greater than the lower bound of the base range of the index type.
{Constraint_Error (raised by failure of run-time check)} The exception
Constraint_Error is raised if either of these checks fails.

        11.a   Ramification:  The checks on the characters need not involve
        more than two checks altogether, since one need only check the
        characters of the string with the lowest and highest position numbers
        against the range of the component subtype.


     NOTES
12   (6) Enumeration literals that are identifiers rather than character_
     literals follow the normal rules for identifiers when used in a name
     (see 4.1 and 4.1.3).  Character_literals used as selector_names follow
     the normal rules for expanded names (see 4.1.3).


                                  Examples

13   Examples of literals:

14
    3.14159_26536    --  a real literal
    1_345            --  an integer literal
    'A'              --  a character literal
    "Some Text"      --  a string literal


                        Incompatibilities With Ada 83

        14.a   {incompatibilities with Ada 83} Because character_literals are
        now treated like other literals, in that they are resolved using
        context rather than depending on direct visibility, additional
        qualification might be necessary when passing a character_literal to
        an overloaded subprogram.

                            Extensions to Ada 83

        14.b   {extensions to Ada 83} Character_literals are now treated
        analogously to null and string_literals, in that they are resolved
        using context, rather than their content; the declaration of the
        corresponding defining_character_literal need not be directly
        visible.

                         Wording Changes From Ada 83

        14.c   Name Resolution rules for enumeration literals that are not
        character_literals are not included anymore, since they are neither
        syntactically nor semantically "literals" but are rather names of
        parameterless functions.



4.3 Aggregates

1   [{aggregate} An aggregate combines component values into a composite
value of an array type, record type, or record extension.]  {literal: see
also aggregate}


                                   Syntax

2   aggregate ::= record_aggregate | extension_aggregate | array_aggregate


                            Name Resolution Rules

3   {expected type [aggregate]} The expected type for an aggregate shall be a
single nonlimited array type, record type, or record extension.

        3.a   Discussion:  See 8.6, ``The Context of Overload Resolution''
        for the meaning of ``shall be a single ... type.''


                               Legality Rules

4   An aggregate shall not be of a class-wide type.

        4.a   Ramification:  When the expected type in some context is
        class-wide, an aggregate has to be explicitly qualified by the
        specific type of value to be created, so that the expected type for
        the aggregate itself is specific.

        4.b   Discussion:  We used to disallow aggregates of a type with
        unknown discriminants.  However, that was unnecessarily restrictive
        in the case of an extension aggregate, and irrelevant to a record
        aggregate (since a type that is legal for a record aggregate could
        not possibly have unknown discriminants) and to an array aggregate
        (the only specific types that can have unknown discriminants are
        private types, private extensions, and types derived from them).


                              Dynamic Semantics

5   {evaluation [aggregate]} For the evaluation of an aggregate, an anonymous
object is created and values for the components or ancestor part are obtained
(as described in the subsequent subclause for each kind of the aggregate) and
assigned into the corresponding components or ancestor part of the anonymous
object.  {assignment operation (during evaluation of an aggregate)} Obtaining
the values and the assignments occur in an arbitrary order.  The value of the
aggregate is the value of this object.

        5.a   Discussion:  The ancestor part is the set of components
        inherited from the ancestor type.  The syntactic category ancestor_
        part is the expression or subtype_mark that specifies how the
        ancestor part of the anonymous object should be initialized.

        5.b   Ramification:  The assignment operations do the necessary value
        adjustment, as described in 7.6.  Note that the value as a whole is
        not adjusted -- just the subcomponents (and ancestor part, if any).
        7.6 also describes when this anonymous object is finalized.

        5.c   If the ancestor_part is a subtype_mark the Initialize procedure
        for the ancestor type is applied to the ancestor part after
        default-initializing it, unless the procedure is abstract, as
        described in 7.6.  The Adjust procedure for the ancestor type is not
        called in this case, since there is no assignment to the ancestor
        part as a whole.

6   {Discriminant_Check [partial]} {check, language-defined (Discriminant_
Check)} If an aggregate is of a tagged type, a check is made that its value
belongs to the first subtype of the type.  {Constraint_Error (raised by
failure of run-time check)} Constraint_Error is raised if this check fails.

        6.a   Ramification:  This check ensures that no values of a tagged
        type are ever outside the first subtype, as required for inherited
        dispatching operations to work properly (see 3.4).  This check will
        always succeed if the first subtype is unconstrained.  This check is
        not extended to untagged types to preserve upward compatibility.


                            Extensions to Ada 83

        6.b   {extensions to Ada 83} We now allow extension_aggregates.

                         Wording Changes From Ada 83

        6.c   We have adopted new wording for expressing the rule that the
        type of an aggregate shall be determinable from the outside, though
        using the fact that it is nonlimited record (extension) or array.

        6.d   An aggregate now creates an anonymous object.  This is
        necessary so that controlled types will work (see 7.6).



4.3.1 Record Aggregates

1   [In a record_aggregate, a value is specified for each component of the
record or record extension value, using either a named or a positional
association.]


                                   Syntax

2   record_aggregate ::= (record_component_association_list)

3   record_component_association_list ::=
        record_component_association {, record_component_association}
      | null record

4   record_component_association ::=
       [ component_choice_list => ] expression

5   component_choice_list ::=
         component_selector_name {| component_selector_name}
       | others

    6   {named component association} A record_component_association is a
    named component association if it has a component_choice_list;
    {positional component association} otherwise, it is a positional
    component association.  Any positional component associations shall
    precede any named component associations.  If there is a named
    association with a component_choice_list of others, it shall come last.

        6.a   Discussion:  These rules were implied by the BNF in an early
        version of the RM9X, but it made the grammar harder to read, and was
        inconsistent with how we handle discriminant constraints.  Note that
        for array aggregates we still express some of the rules in the
        grammar, but array aggregates are significantly different because an
        array aggregate is either all positional (with a possible others at
        the end), or all named.

    7   In the record_component_association_list for a record_aggregate, if
    there is only one association, it shall be a named association.

        7.a   Reason:  Otherwise the construct would be interpreted as a
        parenthesized expression.  This is considered a syntax rule, since it
        is relevant to overload resolution.  We choose not to express it with
        BNF so we can share the definition of record_component_association_
        list in both record_aggregate and extension_aggregate.

        7.b   Ramification:  The record_component_association_list of an
        extension_aggregate does not have such a restriction.
                            Name Resolution Rules

8   {expected type [record_aggregate]} The expected type for a record_
aggregate shall be a single nonlimited record type or record extension.

        8.a   Ramification:  This rule is used to resolve whether an
        aggregate is an array_aggregate or a record_aggregate.  The presence
        of a with is used to resolve between a record_aggregate and an
        extension_aggregate.

9   {needed component (record_aggregate record_component_association_list)}
For the record_component_association_list of a record_aggregate, all
components of the composite value defined by the aggregate are needed[; for
the association list of an extension_aggregate, only those components not
determined by the ancestor expression or subtype are needed (see 4.3.2).]
Each selector_name in a record_component_association shall denote a needed
component [(including possibly a discriminant)].

        9.a   Ramification:  For the association list of a record_aggregate,
        ``needed components'' includes every component of the composite
        value, but does not include those in unchosen variants (see AI-309).
        If there are variants, then the value specified for the discriminant
        that governs them determines which variant is chosen, and hence which
        components are needed.

        9.b   If an extension defines a new known_discriminant_part, then all
        of its discriminants are needed in the component association list of
        an extension aggregate for that type, even if the discriminants have
        the same names and types as discriminants of the type of the ancestor
        expression.  This is necessary to ensure that the positions in the
        record_component_association_list are well defined, and that
        discriminants that govern variant_parts can be given by static
        expressions.

10   {expected type [record_component_association expression]} The expected
type for the expression of a record_component_association is the type of the
associated component(s); {associated components (of a record_component_
association)} the associated component(s) are as follows:

   11  For a positional association, the component [(including possibly
       a discriminant)] in the corresponding relative position (in the
       declarative region of the type), counting only the needed
       components;

 11.a   Ramification:  This means that for an association list of an
        extension_aggregate, only noninherited components are counted to
        determine the position.

   12  For a named association with one or more component_selector_
       names, the named component(s);

   13  For a named association with the reserved word others, all needed
       components that are not associated with some previous
       association.


                               Legality Rules

14   If the type of a record_aggregate is a record extension, then it shall
be a descendant of a record type, through one or more record extensions (and
no private extensions).

15   If there are no components needed in a given record_component_
association_list, then the reserved words null record shall appear rather
than a list of record_component_associations.

        15.a   Ramification:  For example, "(null record)" is a record_
        aggregate for a null record type.  Similarly, "(T'(A) with null
        record)" is an extension_aggregate for a type defined as a null
        record extension of T.

16   Each record_component_association shall have at least one associated
component, and each needed component shall be associated with exactly one
record_component_association.  If a record_component_association has two or
more associated components, all of them shall be of the same type.

        16.a   Ramification:  These rules apply to an association with an
        others choice.

        16.b   Reason:  Without these rules, there would be no way to know
        what was the expected type for the expression of the association.

        16.c   Discussion:  AI-00244 also requires that the expression shall
        be legal for each associated component.  This is because even though
        two components have the same type, they might have different
        subtypes.  Therefore, the legality of the expression, particularly if
        it is an array aggregate, might differ depending on the associated
        component's subtype.  However, we have relaxed the rules on array
        aggregates slightly for Ada 9X, so the staticness of an applicable
        index constraint has no effect on the legality of the array aggregate
        to which it applies.  See 4.3.3.  This was the only case (that we
        know of) where a subtype provided by context affected the legality of
        an expression.

        16.d   Ramification:  The rule that requires at least one associated
        component for each record_component_association implies that there
        can be no extra associations for components that don't exist in the
        composite value, or that are already determined by the ancestor
        expression or subtype of an extension_aggregate.

        16.e   The second part of the first sentence ensures that no needed
        components are left out, nor specified twice.

17   If the components of a variant_part are needed, then the value of a
discriminant that governs the variant_part shall be given by a static
expression.

        17.a   Ramification:  This expression might either be given within
        the aggregate itself, or in a constraint on the parent subtype in a
        derived_type_definition for some ancestor of the type of the
        aggregate.


                              Dynamic Semantics

18   {evaluation [record_aggregate]} The evaluation of a record_aggregate
consists of the evaluation of the record_component_association_list.

19   {evaluation [record_component_association_list]} For the evaluation of a
record_component_association_list, any per-object constraints (see 3.8) for
components specified in the association list are elaborated and any
expressions are evaluated and converted to the subtype of the associated
component.  {implicit subtype conversion [expressions in aggregate]}

        19.a   Ramification:  The conversion might raise Constraint_Error.

        19.b   Discussion:  This check presumably happened as part of the
        dependent compatibility check in Ada 83.

Any constraint elaborations and expression evaluations (and conversions)
occur in an arbitrary order, except that the expression for a discriminant is
evaluated (and converted) prior to the elaboration of any per-object
constraint that depends on it, which in turn occurs prior to the evaluation
and conversion of the expression for the component with the per-object
constraint.

20   The expression of a record_component_association is evaluated (and
converted) once for each associated component.


     NOTES
21   (7) For a record_aggregate with positional associations, expressions
     specifying discriminant values appear first since the known_
     discriminant_part is given first in the declaration of the type; they
     have to be in the same order as in the known_discriminant_part.


                                  Examples

22   Example of a record aggregate with positional associations:

23  (4, July, 1776)                                       --  see 3.8

24   Examples of record aggregates with named associations:

25  (Day => 4, Month => July, Year => 1776)
    (Month => July, Day => 4, Year => 1776)

26  (Disk, Closed, Track => 5, Cylinder => 12)            --  see 3.8.1
    (Unit => Disk, Status => Closed, Cylinder => 9, Track => 1)

27   Example of component association with several choices:

28  (Value => 0, Succ|Pred => new Cell'(0, null, null))   --  see 3.10.1

29   --  The allocator is evaluated twice:  Succ and Pred designate different c\
ells

30   Examples of record aggregates for tagged types (see 3.9 and 3.9.1):

31  Expression'(null record)
    Literal'(Value => 0.0)
    Painted_Point'(0.0, Pi/2.0, Paint => Red)


                            Extensions to Ada 83

        31.a   {extensions to Ada 83} Null record aggregates may now be
        specified, via "(null record)".  However, this syntax is more useful
        for null record extensions in extension aggregates.

                         Wording Changes From Ada 83

        31.b   Various AIs have been incorporated (AI-189, AI-244, and
        AI-309).  In particular, Ada 83 did not explicitly disallow extra
        values in a record aggregate.  Now we do.



4.3.2 Extension Aggregates

1   [An extension_aggregate specifies a value for a type that is a record
extension by specifying a value or subtype for an ancestor of the type,
followed by associations for any components not determined by the ancestor_
part.]


                         Language Design Principles

        1.a   The model underlying this syntax is that a record extension can
        also be viewed as a regular record type with an ancestor "prefix."
        The record_component_association_list corresponds to exactly what
        would be needed if there were no ancestor/prefix type.  The ancestor_
        part determines the value of the ancestor/prefix.

                                   Syntax

2   extension_aggregate ::=
        (ancestor_part with record_component_association_list)

3   ancestor_part ::= expression | subtype_mark


                            Name Resolution Rules

4   {expected type [extension_aggregate]} The expected type for an extension_
aggregate shall be a single nonlimited type that is a record extension.
{expected type [extension_aggregate ancestor expression]} If the ancestor_
part is an expression, it is expected to be of any nonlimited tagged type.

        4.a   Reason:  We could have made the expected type T'Class where T
        is the ultimate ancestor of the type of the aggregate, or we could
        have made it even more specific than that.  However, if the overload
        resolution rules get too complicated, the implementation gets more
        difficult and it becomes harder to produce good error messages.


                               Legality Rules

5   If the ancestor_part is a subtype_mark, it shall denote a specific tagged
subtype.  The type of the extension_aggregate shall be derived from the type
of the ancestor_part, through one or more record extensions (and no private
extensions).


                              Static Semantics

6   {needed component (extension_aggregate record_component_association_
list)} For the record_component_association_list of an extension_aggregate,
the only components needed are those of the composite value defined by the
aggregate that are not inherited from the type of the ancestor_part, plus any
inherited discriminants if the ancestor_part is a subtype_mark that denotes
an unconstrained subtype.


                              Dynamic Semantics

7   {evaluation [extension_aggregate]} For the evaluation of an extension_
aggregate, the record_component_association_list is evaluated.  If the
ancestor_part is an expression, it is also evaluated; if the ancestor_part is
a subtype_mark, the components of the value of the aggregate not given by the
record_component_association_list are initialized by default as for an object
of the ancestor type.  Any implicit initializations or evaluations are
performed in an arbitrary order, except that the expression for a
discriminant is evaluated prior to any other evaluation or initialization
that depends on it.

8   {Discriminant_Check [partial]} {check, language-defined (Discriminant_
Check)} If the type of the ancestor_part has discriminants that are not
inherited by the type of the extension_aggregate, then, unless the ancestor_
part is a subtype_mark that denotes an unconstrained subtype, a check is made
that each discriminant of the ancestor has the value specified for a
corresponding discriminant, either in the record_component_association_list,
or in the derived_type_definition for some ancestor of the type of the
extension_aggregate.  {Constraint_Error (raised by failure of run-time
check)} Constraint_Error is raised if this check fails.

        8.a   Ramification:  Corresponding and specified discriminants are
        defined in 3.7.  The rules requiring static compatibility between new
        discriminants of a derived type and the parent discriminant(s) they
        constrain ensure that at most one check is required per discriminant
        of the ancestor expression.


     NOTES
9    (8) If all components of the value of the extension_aggregate are
     determined by the ancestor_part, then the record_component_association_
     list is required to be simply null record.

10   (9) If the ancestor_part is a subtype_mark, then its type can be
     abstract.  If its type is controlled, then as the last step of
     evaluating the aggregate, the Initialize procedure of the ancestor type
     is called, unless the Initialize procedure is abstract (see 7.6).


                                  Examples

11   Examples of extension aggregates (for types defined in 3.9.1):

12  Painted_Point'(Point with Red)
    (Point'(P) with Paint => Black)

13  (Expression with Left => 1.2, Right => 3.4)
    Addition'(Binop with null record)
                 -- presuming Binop is of type Binary_Operation


                            Extensions to Ada 83

        13.a   {extensions to Ada 83} The extension aggregate syntax is new.



4.3.3 Array Aggregates

1   [In an array_aggregate, a value is specified for each component of an
array, either positionally or by its index.]  For a positional_array_
aggregate, the components are given in increasing-index order, with a final
others, if any, representing any remaining components.  For a named_array_
aggregate, the components are identified by the values covered by the
discrete_choices.  {94-4603.a}


                         Language Design Principles

        1.a   The rules in this subclause are based on terms and rules for
        discrete_choice_lists defined in 3.8.1, ``Variant Parts and Discrete
        Choices''.

                                   Syntax

2   array_aggregate ::=
      positional_array_aggregate | named_array_aggregate

3   positional_array_aggregate ::=
        (expression, expression {, expression})
      | (expression {, expression}, others => expression)

4   named_array_aggregate ::=
        (array_component_association {, array_component_association})

5   array_component_association ::=
        discrete_choice_list => expression


6   {n-dimensional array_aggregate} An n-dimensional array_aggregate is one
that is written as n levels of nested array_aggregates (or at the bottom
level, equivalent string_literals).  {subaggregate (of an array_aggregate)}
For the multidimensional case (n >= 2) the array_aggregates (or equivalent
string_literals) at the n-1 lower levels are called subaggregates of the
enclosing n-dimensional array_aggregate.  {array component expression} The
expressions of the bottom level subaggregates (or of the array_aggregate
itself if one-dimensional) are called the array component expressions of the
enclosing n-dimensional array_aggregate.

        6.a   Ramification:  Subaggregates do not have a type.  They
        correspond to part of an array.  For example, with a matrix, a
        subaggregate would correspond to a single row of the matrix.  The
        definition of "n-dimensional" array_aggregate applies to sub-
        aggregates as well as aggregates that have a type.

        6.b   To be honest:  {others choice} An others choice is the reserved
        word others as it appears in a positional_array_aggregate or as the
        discrete_choice of the discrete_choice_list in an array_component_
        association.


                            Name Resolution Rules

7   {expected type [array_aggregate]} The expected type for an array_
aggregate (that is not a subaggregate) shall be a single nonlimited array
type.  {expected type [array_aggregate component expression]} The component
type of this array type is the expected type for each array component
expression of the array_aggregate.

        7.a   Ramification:  We already require a single array or record type
        or record extension for an aggregate.  The above rule requiring a
        single nonlimited array type (and similar ones for record and
        extension aggregates) resolves which kind of aggregate you have.

8   {expected type [array_aggregate discrete_choice]} The expected type for
each discrete_choice in any discrete_choice_list of a named_array_aggregate
is the type of the corresponding index; {corresponding index (for an array_
aggregate)} the corresponding index for an array_aggregate that is not a
subaggregate is the first index of its type; for an (n-m)-dimensional
subaggregate within an array_aggregate of an n-dimensional type, the
corresponding index is the index in position m+1.


                               Legality Rules

9   An array_aggregate of an n-dimensional array type shall be written as an
n-dimensional array_aggregate.

        9.a   Ramification:  In an m-dimensional array_aggregate [(including
        a subaggregate)], where m >= 2, each of the expressions has to be an
        (m-1)-dimensional subaggregate.

10   An others choice is allowed for an array_aggregate only if an applicable
index constraint applies to the array_aggregate.  {applicable index
constraint} [An applicable index constraint is a constraint provided by
certain contexts where an array_aggregate is permitted that can be used to
determine the bounds of the array value specified by the aggregate.]  Each of
the following contexts (and none other) defines an applicable index
constraint:

   11  For an explicit_actual_parameter, an explicit_generic_actual_
       parameter, the expression of a return_statement, the initializa-
       tion expression in an object_declaration, or a default_expression
       [(for a parameter or a component)], when the nominal subtype of
       the corresponding formal parameter, generic formal parameter,
       function result, object, or component is a constrained array
       subtype, the applicable index constraint is the constraint of the
       subtype;

   12  For the expression of an assignment_statement where the name
       denotes an array variable, the applicable index constraint is the
       constraint of the array variable;

 12.a   Reason:  This case is broken out because the constraint comes
        from the actual subtype of the variable (which is always
        constrained) rather than its nominal subtype (which might be
        unconstrained).

   13  For the operand of a qualified_expression whose subtype_mark
       denotes a constrained array subtype, the applicable index
       constraint is the constraint of the subtype;

   14  For a component expression in an aggregate, if the component's
       nominal subtype is a constrained array subtype, the applicable
       index constraint is the constraint of the subtype;

 14.a   Discussion:  Here, the array_aggregate with others is being used
        within a larger aggregate.

   15  For a parenthesized expression, the applicable index constraint
       is that, if any, defined for the expression.

 15.a   Discussion:  RM83 omitted this case, presumably as an oversight.
        We want to minimize situations where an expression becomes
        illegal if parenthesized.

16   The applicable index constraint applies to an array_aggregate that
appears in such a context, as well as to any subaggregates thereof.  In the
case of an explicit_actual_parameter (or default_expression) for a call on a
generic formal subprogram, no applicable index constraint is defined.

        16.a   Reason:  This avoids generic contract model problems, because
        only mode conformance is required when matching actual subprograms
        with generic formal subprograms.

17   The discrete_choice_list of an array_component_association is allowed to
have a discrete_choice that is a nonstatic expression or that is a discrete_
range that defines a nonstatic or null range, only if it is the single
discrete_choice of its discrete_choice_list, and there is only one array_
component_association in the array_aggregate.

        17.a   Discussion:  We now allow a nonstatic others choice even if
        there are other array component expressions as well.

18   In a named_array_aggregate with more than one discrete_choice, no two
discrete_choices are allowed to cover the same value (see 3.8.1); if there is
no others choice, the discrete_choices taken together shall exactly cover a
contiguous sequence of values of the corresponding index type.

        18.a   Ramification:  This implies that each component must be
        specified exactly once.  See AI-309.

19   A bottom level subaggregate of a multidimensional array_aggregate of a
given array type is allowed to be a string_literal only if the component type
of the array type is a character type; each character of such a string_
literal shall correspond to a defining_character_literal of the component
type.


                              Static Semantics

20   A subaggregate that is a string_literal is equivalent to one that is a
positional_array_aggregate of the same length, with each expression being the
character_literal for the corresponding character of the string_literal.


                              Dynamic Semantics

21   {evaluation [array_aggregate]} The evaluation of an array_aggregate of a
given array type proceeds in two steps:

   22  Any discrete_choices of this aggregate and of its subaggregates
       are evaluated in an arbitrary order, and converted to the
       corresponding index type; {implicit subtype conversion [choices
       of aggregate]}

   23  The array component expressions of the aggregate are evaluated in
       an arbitrary order and their values are converted to the
       component subtype of the array type; an array component
       expression is evaluated once for each associated component.
       {implicit subtype conversion [expressions of aggregate]}

        23.a   Ramification:  Subaggregates are not separately evaluated.
        The conversion of the value of the component expressions to the
        component subtype might raise Constraint_Error.

24   {bounds (of the index range of an array_aggregate)} The bounds of the
index range of an array_aggregate [(including a subaggregate)] are determined
as follows:

   25  For an array_aggregate with an others choice, the bounds are
       those of the corresponding index range from the applicable index
       constraint;

   26  For a positional_array_aggregate [(or equivalent string_literal)]
       without an others choice, the lower bound is that of the
       corresponding index range in the applicable index constraint, if
       defined, or that of the corresponding index subtype, if not; in
       either case, the upper bound is determined from the lower bound
       and the number of expressions [(or the length of the string_
       literal)];

   27  For a named_array_aggregate without an others choice, the bounds
       are determined by the smallest and largest index values covered
       by any discrete_choice_list.

 27.a   Reason:  We don't need to say that each index value has to be
        covered exactly once, since that is a ramification of the
        general rule on aggregates that each component's value has to be
        specified exactly once.

28   {Range_Check [partial]} {check, language-defined (Range_Check)} For an
array_aggregate, a check is made that the index range defined by its bounds
is compatible with the corresponding index subtype.

        28.a   Discussion:  In RM83, this was phrased more explicitly, but
        once we define "compatibility" between a range and a subtype, it
        seems to make sense to take advantage of that definition.

        28.b   Ramification:  The definition of compatibility handles the
        special case of a null range, which is always compatible with a
        subtype.  See AI-00313.

29   {Index_Check [partial]} {check, language-defined (Index_Check)} For an
array_aggregate with an others choice, a check is made that no expression is
specified for an index value outside the bounds determined by the applicable
index constraint.

        29.a   Discussion:  RM83 omitted this case, apparently through an
        oversight.  AI-309 defines this as a dynamic check, even though other
        Ada 83 rules ensured that this check could be performed statically.
        We now allow an others choice to be dynamic, even if it is not the
        only choice, so this check now needs to be dynamic, in some cases.
        Also, within a generic unit, this would be a nonstatic check in some
        cases.

30   {Index_Check [partial]} {check, language-defined (Index_Check)} For a
multidimensional array_aggregate, a check is made that all subaggregates that
correspond to the same index have the same bounds.

        30.a   Ramification:  No array bounds ``sliding'' is performed on
        subaggregates.

        30.b   Reason:  If sliding were performed, it would not be obvious
        which subaggregate would determine the bounds of the corresponding
        index.

31   {Constraint_Error (raised by failure of run-time check)} The exception
Constraint_Error is raised if any of the above checks fail.


     NOTES
32   (10) In an array_aggregate, positional notation may only be used with
     two or more expressions; a single expression in parentheses is
     interpreted as a parenthesized_expression.  A named_array_aggregate,
     such as (1 => X), may be used to specify an array with a single
     component.


                                  Examples

33   Examples of array aggregates with positional associations:

34  (7, 9, 5, 1, 3, 2, 4, 8, 6, 0)
    Table'(5, 8, 4, 1, others => 0)  --  see 3.6

35   Examples of array aggregates with named associations:

36  (1 .. 5 => (1 .. 8 => 0.0))      --  two-dimensional
    (1 .. N => new Cell)             --  N new cells, in particular for N = 0

37  Table'(2 | 4 | 10 => 1, others => 0)
    Schedule'(Mon .. Fri => True,  others => False)  --  see 3.6
    Schedule'(Wed | Sun  => False, others => True)
    Vector'(1 => 2.5)                                --  single-component vector

38   Examples of two-dimensional array aggregates:

39  -- Three aggregates for the same value of subtype Matrix(1..2,1..3) (see 3.\
6):

40  ((1.1, 1.2, 1.3), (2.1, 2.2, 2.3))
    (1 => (1.1, 1.2, 1.3), 2 => (2.1, 2.2, 2.3))
    (1 => (1 => 1.1, 2 => 1.2, 3 => 1.3), 2 => (1 => 2.1, 2 => 2.2, 3 => 2.3))

41   Examples of aggregates as initial values:

42  A : Table := (7, 9, 5, 1, 3, 2, 4, 8, 6, 0);        -- A(1)=7, A(10)=0{94-4\
667.c}
    B : Table := (2 | 4 | 10 => 1, others => 0);        -- B(1)=0, B(10)=1
    C : constant Matrix := (1 .. 5 => (1 .. 8 => 0.0)); -- C'Last(1)=5, C'Last(\
2)=8

43  D : Bit_Vector(M .. N) := (M .. N => True);         -- see 3.6
    E : Bit_Vector(M .. N) := (others => True);
    F : String(1 .. 1) := (1 => 'F');  -- a one component aggregate: same as "F"
                            Extensions to Ada 83

        43.a   {extensions to Ada 83} We now allow "named with others"
        aggregates in all contexts where there is an applicable index
        constraint, effectively eliminating what was RM83-4.3.2(6).  Sliding
        never occurs on an aggregate with others, because its bounds come
        from the applicable index constraint, and therefore already match the
        bounds of the target.

        43.b   The legality of an others choice is no longer affected by the
        staticness of the applicable index constraint.  This substantially
        simplifies several rules, while being slightly more flexible for the
        user.  It obviates the rulings of AI-244 and AI-310, while taking
        advantage of the dynamic nature of the "extra values" check required
        by AI-309.

        43.c   Named array aggregates are permitted even if the index type is
        descended from a formal scalar type.  See 4.9 and AI-00190.

                         Wording Changes From Ada 83

        43.d   We now separate named and positional array aggregate syntax,
        since, unlike other aggregates, named and positional associations
        cannot be mixed in array aggregates (except that an others choice is
        allowed in a positional array aggregate).

        43.e   We have also reorganized the presentation to handle
        multidimensional and one-dimensional aggregates more uniformly, and
        to incorporate the rulings of AI-19, AI-309, etc.



4.4 Expressions

1   {expression} An expression is a formula that defines the computation or
retrieval of a value.  In this International Standard, the term
``expression'' refers to a construct of the syntactic category expression or
of any of the other five syntactic categories defined below.  {and operator}
{operator (and)} {or operator} {operator (or)} {xor operator} {operator
(xor)} {and then (short-circuit control form)} {or else (short-circuit
control form)} {= operator} {operator (=)} {equal operator} {operator
(equal)} {/= operator} {operator (/=)} {not equal operator} {operator (not
equal)} {< operator} {operator (<)} {less than operator} {operator (less
than)} {<= operator} {operator (<=)} {less than or equal operator} {operator
(less than or equal)} {> operator} {operator (>)} {greater than operator}
{operator (greater than)} {>= operator} {operator (>=)} {greater than or
equal operator} {operator (greater than or equal)} {in (membership test)}
{not in (membership test)} {+ operator} {operator (+)} {plus operator}
{operator (plus)} {- operator} {operator (-)} {minus operator} {operator
(minus)} {& operator} {operator (&)} {ampersand operator} {operator
(ampersand)} {concatenation operator} {operator (concatenation)} {catenation
operator: see concatenation operator} {* operator} {operator (*)} {multiply
operator} {operator (multiply)} {times operator} {operator (times)} {/
operator} {operator (/)} {divide operator} {operator (divide)} {mod operator}
{operator (mod)} {rem operator} {operator (rem)} {** operator} {operator
(**)} {exponentiation operator} {operator (exponentiation)} {abs operator}
{operator (abs)} {absolute value} {not operator} {operator (not)}


                                   Syntax

2   expression ::=
         relation {and relation} | relation {and then relation}
       | relation {or relation}  | relation {or else relation}
       | relation {xor relation}

3   relation ::=
         simple_expression [relational_operator simple_expression]
       | simple_expression [not] in range
       | simple_expression [not] in subtype_mark

4   simple_expression ::= [unary_adding_operator] term {binary_adding_operator \
term}

5   term ::= factor {multiplying_operator factor}

6   factor ::= primary [** primary] | abs primary | not primary

7   primary ::=
       numeric_literal | null | string_literal | aggregate
     | name | qualified_expression | allocator | (expression)


                            Name Resolution Rules

8   A name used as a primary shall resolve to denote an object or a value.

        8.a   Discussion:  This replaces RM83-4.4(3).  We don't need to
        mention named numbers explicitly, because the name of a named number
        denotes a value.  We don't need to mention attributes explicitly,
        because attributes now denote (rather than yield) values in general.
        Also, the new wording allows attributes that denote objects, which
        should always have been allowed (in case the implementation chose to
        have such a thing).

        8.b   Reason:  It might seem odd that this is an overload resolution
        rule, but it is relevant during overload resolution.  For example, it
        helps ensure that a primary that consists of only the identifier of a
        parameterless function is interpreted as a function_call rather than
        directly as a direct_name.


                              Static Semantics

9   Each expression has a type; it specifies the computation or retrieval of
a value of that type.


                              Dynamic Semantics

10   {evaluation [primary that is a name]} The value of a primary that is a
name denoting an object is the value of the object.


                         Implementation Permissions

11   {Overflow_Check [partial]} {check, language-defined (Overflow_Check)}
{Constraint_Error (raised by failure of run-time check)} For the evaluation
of a primary that is a name denoting an object of an unconstrained numeric
subtype, if the value of the object is outside the base range of its type,
the implementation may either raise Constraint_Error or return the value of
the object.

        11.a   Ramification:  This means that if extra-range intermediates
        are used to hold the value of an object of an unconstrained numeric
        subtype, a Constraint_Error can be raised on a read of the object,
        rather than only on an assignment to it.  Similarly, it means that
        computing the value of an object of such a subtype can be deferred
        until the first read of the object (presuming no side-effects other
        than failing an Overflow_Check are possible).  This permission is
        over and above that provided by clause 11.6, since this allows the
        Constraint_Error to move to a different handler.

        11.b   Reason:  This permission is intended to allow extra-range
        registers to be used efficiently to hold parameters and local
        variables, even if they might need to be transferred into smaller
        registers for performing certain predefined operations.

        11.c   Discussion:  There is no need to mention other kinds of
        primarys, since any Constraint_Error to be raised can be ``charged''
        to the evaluation of the particular kind of primary.


                                  Examples

12   Examples of primaries:

13  4.0                --  real literal
    Pi                 --  named number
    (1 .. 10 => 0)     --  array aggregate
    Sum                --  variable
    Integer'Last       --  attribute
    Sine(X)            --  function call
    Color'(Blue)       --  qualified expression
    Real(M*N)          --  conversion
    (Line_Count + 10)  --  parenthesized expression

14   Examples of expressions:

15  Volume                      -- primary
    not Destroyed               -- factor
    2*Line_Count                -- term
    -4.0                        -- simple expression
    -4.0 + A                    -- simple expression
    B**2 - 4.0*A*C              -- simple expression
    Password(1 .. 3) = "Bwv"    -- relation
    Count in Small_Int          -- relation
    Count not in Small_Int      -- relation
    Index = 0 or Item_Hit       -- expression
    (Cold and Sunny) or Warm    -- expression (parentheses are required)
    A**(B**C)                   -- expression (parentheses are required)


                            Extensions to Ada 83

        15.a   {extensions to Ada 83} In Ada 83, out parameters and their
        nondiscriminant subcomponents are not allowed as primaries.  These
        restrictions are eliminated in Ada 9X.

        15.b   In various contexts throughout the language where Ada 83
        syntax rules had simple_expression, the corresponding Ada 9X syntax
        rule has expression instead.  This reflects the inclusion of modular
        integer types, which makes the logical operators "and", "or", and
        "xor" more useful in expressions of an integer type.  Requiring
        parentheses to use these operators in such contexts seemed
        unnecessary and potentially confusing.  Note that the bounds of a
        range still have to be specified by simple_expressions, since
        otherwise expressions involving membership tests might be ambiguous.
        Essentially, the operation ".." is of higher precedence than the
        logical operators, and hence uses of logical operators still have to
        be parenthesized when used in a bound of a range.



4.5 Operators and Expression Evaluation

1   [{precedence of operators} {operator precedence} The language defines the
following six categories of operators (given in order of increasing
precedence).  The corresponding operator_symbols, and only those, can be used
as designators in declarations of functions for user-defined operators.  See
6.6, ``Overloading of Operators''.]
                                   Syntax

2   logical_operator                                      ::=  and | or  | xor

3   relational_operator                                   ::=  =   | /=  | <   \
| <= | > | >=

4   binary_adding_operator                                ::=  +   | -   | &

5   unary_adding_operator                                 ::=  +   | -

6   multiplying_operator                                  ::=  *   | /   | mod \
| rem

7   highest_precedence_operator                           ::=  **  | abs | not

        7.a   Discussion:  Some of the above syntactic categories are not
        used in other syntax rules.  They are just used for classification.
        The others are used for both classification and parsing.


                              Static Semantics

8   For a sequence of operators of the same precedence level, the operators
are associated with their operands in textual order from left to right.
Parentheses can be used to impose specific associations.

        8.a   Discussion:  The left-associativity is not directly inherent in
        the grammar of 4.4, though in 1.1.4 the definition of the metasymbols
        {} implies left associativity.  So this could be seen as redundant,
        depending on how literally one interprets the definition of the {}
        metasymbols.

        8.b   See the Implementation Permissions below regarding flexibility
        in reassociating operators of the same precedence.

9   {predefined operator} {operator (predefined)} For each form of type
definition, certain of the above operators are predefined; that is, they are
implicitly declared immediately after the type definition.  {binary operator}
{operator (binary)} {unary operator} {operator (unary)} For each such
implicit operator declaration, the parameters are called Left and Right for
binary operators; the single parameter is called Right for unary operators.
[An expression of the form X op Y, where op is a binary operator, is
equivalent to a function_call of the form "op"(X, Y).  An expression of the
form op Y, where op is a unary operator, is equivalent to a function_call of
the form "op"(Y).  The predefined operators and their effects are described
in subclauses 4.5.1 through 4.5.6.]


                              Dynamic Semantics

10   [{Constraint_Error (raised by failure of run-time check)} The predefined
operations on integer types either yield the mathematically correct result or
raise the exception Constraint_Error.  For implementations that support the
Numerics Annex, the predefined operations on real types yield results whose
accuracy is defined in Annex G, or raise the exception Constraint_Error.
{94-4481.a}]

        10.a   To be honest:  Predefined operations on real types can
        ``silently'' give wrong results when the Machine_Overflows attribute
        is false, and the computation overflows.


                         Implementation Requirements

11   {Constraint_Error (raised by failure of run-time check)} The
implementation of a predefined operator that delivers a result of an integer
or fixed point type may raise Constraint_Error only if the result is outside
the base range of the result type.

12   {Constraint_Error (raised by failure of run-time check)} The
implementation of a predefined operator that delivers a result of a floating
point type may raise Constraint_Error only if the result is outside the safe
range of the result type.

        12.a   To be honest:  An exception is made for exponentiation by a
        negative exponent in 4.5.6.


                         Implementation Permissions

13   For a sequence of predefined operators of the same precedence level (and
in the absence of parentheses imposing a specific association), an
implementation may impose any association of the operators with operands so
long as the result produced is an allowed result for the left-to-right
association, but ignoring the potential for failure of language-defined
checks in either the left-to-right or chosen order of association.

        13.a   Discussion:  Note that the permission to reassociate the
        operands in any way subject to producing a result allowed for the
        left-to-right association is not much help for most floating point
        operators, since reassociation may introduce significantly different
        round-off errors, delivering a result that is outside the model
        interval for the left-to-right association.  Similar problems arise
        for division with integer or fixed point operands.

        13.b   Note that this permission does not apply to user-defined
        operators.


     NOTES
14   (11) The two operands of an expression of the form X op Y, where op is a
     binary operator, are evaluated in an arbitrary order, as for any
     function_call (see 6.4).


                                  Examples

15   Examples of precedence:

16  not Sunny or Warm    --  same as (not Sunny) or Warm
    X > 4.0 and Y > 0.0  --  same as (X > 4.0) and (Y > 0.0)

17  -4.0*A**2            --  same as -(4.0 * (A**2))
    abs(1 + A) + B       --  same as (abs (1 + A)) + B
    Y**(-3)              --  parentheses are necessary
    A / B * C            --  same as (A/B)*C
    A + (B + C)          --  evaluate B + C before adding it to A


                         Wording Changes From Ada 83

        17.a   We don't give a detailed definition of precedence, since it is
        all implicit in the syntax rules anyway.

        17.b   The permission to reassociate is moved here from RM83-11.6(5),
        so it is closer to the rules defining operator association.



4.5.1 Logical Operators and Short-circuit Control Forms

                            Name Resolution Rules

1   {short-circuit control form} {and then (short-circuit control form)} {or
else (short-circuit control form)} An expression consisting of two relations
connected by and then or or else (a short-circuit control form) shall resolve
to be of some boolean type; {expected type [short-circuit control form
relation]} the expected type for both relations is that same boolean type.

        1.a   Reason:  This rule is written this way so that overload
        resolution treats the two operands symmetrically; the resolution of
        overloading present in either one can benefit from the resolution of
        the other.  Furthermore, the type expected by context can help.


                              Static Semantics

2   {logical operator} {operator (logical)} {and operator} {operator (and)}
{or operator} {operator (or)} {xor operator} {operator (xor)} The following
logical operators are predefined for every boolean type T, for every modular
type T, and for every one-dimensional array type T whose component type is a
boolean type:  {bit string: see logical operators on boolean arrays}

3
    function "and"(Left, Right : T) return T
    function "or" (Left, Right : T) return T
    function "xor"(Left, Right : T) return T

        3.a   To be honest:  For predefined operators, the parameter and
        result subtypes shown as T are actually the unconstrained subtype of
        the type.

4   For boolean types, the predefined logical operators and, or, and xor
perform the conventional operations of conjunction, inclusive disjunction,
and exclusive disjunction, respectively.

5   For modular types, the predefined logical operators are defined on a
bit-by-bit basis, using the binary representation of the value of the
operands to yield a binary representation for the result, where zero
represents False and one represents True.  If this result is outside the base
range of the type, a final subtraction by the modulus is performed to bring
the result into the base range of the type.

6   The logical operators on arrays are performed on a component-by-component
basis on matching components (as for equality -- see 4.5.2), using the
predefined logical operator for the component type.  The bounds of the
resulting array are those of the left operand.


                              Dynamic Semantics

7   {evaluation [short-circuit control form]} The short-circuit control forms
and then and or else deliver the same result as the corresponding predefined
and and or operators for boolean types, except that the left operand is
always evaluated first, and the right operand is not evaluated if the value
of the left operand determines the result.

8   {Length_Check [partial]} {check, language-defined (Length_Check)} For the
logical operators on arrays, a check is made that for each component of the
left operand there is a matching component of the right operand, and vice
versa.  {Range_Check [partial]} {check, language-defined (Range_Check)} Also,
a check is made that each component of the result belongs to the component
subtype.  {Constraint_Error (raised by failure of run-time check)} The
exception Constraint_Error is raised if either of the above checks fails.

        8.a   Discussion:  The check against the component subtype is per
        AI-00535.
     NOTES
9    (12) The conventional meaning of the logical operators is given by the
     following truth table:

10
                A               B           (A and B)        (A or B)       (A \
xor B)

                 True            True            True            True          \
  False
                 True            False           False           True          \
  True
                 False           True            False           True          \
  True
                 False           False           False           False         \
  False


                                  Examples

11   Examples of logical operators:

12  Sunny or Warm
    Filter(1 .. 10) and Filter(15 .. 24)   --   see 3.6.1

13   Examples of short-circuit control forms:

14  Next_Car.Owner /= null and then Next_Car.Owner.Age > 25   --   see 3.10.1
    N = 0 or else A(N) = Hit_Value



4.5.2 Relational Operators and Membership Tests

1   [{relational operator} {operator (relational)} {comparison operator: see
relational operator} {equality operator} {operator (equality)} The equality
operators = (equals) and /= (not equals) are predefined for nonlimited types.
{ordering operator} {operator (ordering)} The other relational_operators are
the ordering operators < (less than), <= (less than or equal), > (greater
than), and >= (greater than or equal).  {= operator} {operator (=)} {equal
operator} {operator (equal)} {/= operator} {operator (/=)} {not equal
operator} {operator (not equal)} {< operator} {operator (<)} {less than
operator} {operator (less than)} {<= operator} {operator (<=)} {less than or
equal operator} {operator (less than or equal)} {> operator} {operator (>)}
{greater than operator} {operator (greater than)} {>= operator} {operator
(>=)} {greater than or equal operator} {operator (greater than or equal)}
{discrete array type} The ordering operators are predefined for scalar types,
and for discrete array types, that is, one-dimensional array types whose
components are of a discrete type.

        1.a   Ramification:  The equality operators are not defined for every
        nonlimited type -- see below for the exact rule.

2   {membership test} {in (membership test)} {not in (membership test)} A
membership test, using in or not in, determines whether or not a value
belongs to a given subtype or range, or has a tag that identifies a type that
is covered by a given type.  Membership tests are allowed for all types.]


                            Name Resolution Rules

3   {expected type [membership test simple_expression]} {tested type (of a
membership test)} The tested type of a membership test is the type of the
range or the type determined by the subtype_mark.  If the tested type is
tagged, then the simple_expression shall resolve to be of a type that covers
or is covered by the tested type; if untagged, the expected type for the
simple_expression is the tested type.

        3.a   Reason:  The part of the rule for untagged types is stated in a
        way that ensures that operands like null are still legal as operands
        of a membership test.

        3.b   The significance of ``covers or is covered by'' is that we
        allow the simple_expression to be of any class-wide type that covers
        the tested type, not just the one rooted at the tested type.


                               Legality Rules

4   For a membership test, if the simple_expression is of a tagged class-wide
type, then the tested type shall be (visibly) tagged.

        4.a   Ramification:  Untagged types covered by the tagged class-wide
        type are not permitted.  Such types can exist if they are descendants
        of a private type whose full type is tagged.  This rule is intended
        to avoid confusion since such derivatives don't have their ``own''
        tag, and hence are indistinguishable from one another at run time
        once converted to a covering class-wide type.


                              Static Semantics

5   The result type of a membership test is the predefined type Boolean.

6   The equality operators are predefined for every specific type T that is
not limited, and not an anonymous access type, with the following
specifications:

7   function "=" (Left, Right : T) return Boolean
    function "/="(Left, Right : T) return Boolean

8   The ordering operators are predefined for every specific scalar type T,
and for every discrete array type T, with the following specifications:

9   function "<" (Left, Right : T) return Boolean
    function "<="(Left, Right : T) return Boolean
    function ">" (Left, Right : T) return Boolean
    function ">="(Left, Right : T) return Boolean


                              Dynamic Semantics

10   For discrete types, the predefined relational operators are defined in
terms of corresponding mathematical operations on the position numbers of the
values of the operands.

11   For real types, the predefined relational operators are defined in terms
of the corresponding mathematical operations on the values of the operands,
subject to the accuracy of the type.

        11.a   Ramification:  For floating point types, the results of
        comparing nearly equal values depends on the accuracy of the
        implementation (see G.2.1, ``Model of Floating Point Arithmetic'' for
        implementations that support the Numerics Annex).  {94-4481.a}

        11.b   Implementation Note:  On a machine with signed zeros, if the
        generated code generates both plus zero and minus zero, plus and
        minus zero must be equal by the predefined equality operators.
        {94-4539.c}

12   Two access-to-object values are equal if they designate the same object,
or if both are equal to the null value of the access type.

13   Two access-to-subprogram values are equal if they are the result of the
same evaluation of an Access attribute_reference, or if both are equal to the
null value of the access type.  Two access-to-subprogram values are unequal
if they designate different subprograms.  {unspecified [partial]} [It is
unspecified whether two access values that designate the same subprogram but
are the result of distinct evaluations of Access attribute_references are
equal or unequal.]

        13.a   Reason:  This allows each Access attribute_reference for a
        subprogram to designate a distinct ``wrapper'' subprogram if
        necessary to support an indirect call.

14   {equality operator (special inheritance rule for tagged types)} For a
type extension, predefined equality is defined in terms of the primitive
[(possibly user-defined)] equals operator of the parent type and of any
tagged components of the extension part, and predefined equality for any
other components not inherited from the parent type.

        14.a   Ramification:  Two values of a type extension are not equal if
        there is a variant_part in the extension part and the two values have
        different variants present.  This is a ramification of the
        requirement that a discriminant governing such a variant_part has to
        be a ``new'' discriminant, and so has to be equal in the two values
        for the values to be equal.  Note that variant_parts in the parent
        part need not match if the primitive equals operator for the parent
        type considers them equal.

15   For a private type, if its full type is tagged, predefined equality is
defined in terms of the primitive equals operator of the full type; if the
full type is untagged, predefined equality for the private type is that of
its full type.

16   {matching components} For other composite types, the predefined equality
operators [(and certain other predefined operations on composite types -- see
4.5.1 and 4.6)] are defined in terms of the corresponding operation on
matching components, defined as follows:

   17  For two composite objects or values of the same non-array type,
       matching components are those that correspond to the same
       component_declaration or discriminant_specification; {94-4667.f}

   18  For two one-dimensional arrays of the same type, matching
       components are those (if any) whose index values match in the
       following sense: the lower bounds of the index ranges are defined
       to match, and the successors of matching indices are defined to
       match;

   19  For two multidimensional arrays of the same type, matching
       components are those whose index values match in successive index
       positions.

20   The analogous definitions apply if the types of the two objects or
values are convertible, rather than being the same.

        20.a   Discussion:  Ada 83 seems to omit this part of the definition,
        though it is used in array type conversions.  See 4.6.

21   Given the above definition of matching components, the result of the
predefined equals operator for composite types (other than for those
composite types covered earlier) is defined as follows:

   22  If there are no components, the result is defined to be True;

   23  If there are unmatched components, the result is defined to be
       False;

   24  Otherwise, the result is defined in terms of the primitive equals
       operator for any matching tagged components, and the predefined
       equals for any matching untagged components.

 24.a   Reason:  This asymmetry between tagged and untagged components
        is necessary to preserve upward compatibility and corresponds
        with the corresponding situation with generics, where the
        predefined operations ``reemerge'' in a generic for untagged
        types, but do not for tagged types.  Also, only tagged types
        support user-defined assignment (see 7.6), so only tagged types
        can fully handle levels of indirection in the implementation of
        the type.  For untagged types, one reason for a user-defined
        equals operator might be to allow values with different bounds
        or discriminants to compare equal in certain cases.  When such
        values are matching components, the bounds or discriminants will
        necessarily match anyway if the discriminants of the enclosing
        values match.

        24.b   Ramification:  Two null arrays of the same type are always
        equal; two null records of the same type are always equal.

        24.c   Note that if a composite object has a component of a floating
        point type, and the floating point type has both a plus and minus
        zero, which are considered equal by the predefined equality, then a
        block compare cannot be used for the predefined composite equality.
        Of course, with user-defined equals operators for tagged components,
        a block compare breaks down anyway, so this is not the only special
        case that requires component-by-component comparisons.  On a one's
        complement machine, a similar situation might occur for integer
        types, since one's complement machines typically have both a plus and
        minus (integer) zero.

25   The predefined "/=" operator gives the complementary result to the
predefined "=" operator.

        25.a   Ramification:  Furthermore, if the user defines an "="
        operator that returns Boolean, then a "/=" operator is implicitly
        declared in terms of the user-defined "=" operator so as to give the
        complementary result.  See 6.6.

26   {lexicographic order} For a discrete array type, the predefined ordering
operators correspond to lexicographic order using the predefined order
relation of the component type:  A null array is lexicographically less than
any array having at least one component.  In the case of nonnull arrays, the
left operand is lexicographically less than the right operand if the first
component of the left operand is less than that of the right; otherwise the
left operand is lexicographically less than the right operand only if their
first components are equal and the tail of the left operand is
lexicographically less than that of the right (the tail consists of the
remaining components beyond the first and can be null).

27   {evaluation [membership test]} For the evaluation of a membership test,
the simple_expression and the range (if any) are evaluated in an arbitrary
order.

28   A membership test using in yields the result True if:

   29  The tested type is scalar, and the value of the simple_expression
       belongs to the given range, or the range of the named subtype; or

 29.a   Ramification:  The scalar membership test only does a range
        check.  It does not perform any other check, such as whether a
        value falls in a ``hole'' of a ``holey'' enumeration type.  The
        Pos attribute function can be used for that purpose.

 29.b   Even though Standard.Float is an unconstrained subtype, the test
        ``X in Float'' will still return False (presuming the evaluation
        of X does not raise Constraint_Error) when X is outside
        Float'Range.

   30  The tested type is not scalar, and the value of the simple_
       expression satisfies any constraints of the named subtype, and,
       if the type of the simple_expression is class-wide, the value has
       a tag that identifies a type covered by the tested type.

 30.a   Ramification:  Note that the tag is not checked if the simple_
        expression is of a specific type.

31   Otherwise the test yields the result False.

32   A membership test using not in gives the complementary result to the
corresponding membership test using in.


     NOTES
33   (13) No exception is ever raised by a membership test, by a predefined
     ordering operator, or by a predefined equality operator for an
     elementary type, but an exception can be raised by the evaluation of the
     operands.  A predefined equality operator for a composite type can only
     raise an exception if the type has a tagged part whose primitive equals
     operator propagates an exception.

34   (14) If a composite type has components that depend on discriminants,
     two values of this type have matching components if and only if their
     discriminants are equal.  Two nonnull arrays have matching components if
     and only if the length of each dimension is the same for both.


                                  Examples

35   Examples of expressions involving relational operators and membership
tests:

36  X /= Y

37  "" < "A" and "A" < "Aa"     --  True
    "Aa" < "B" and "A" < "A  "  --  True

38  My_Car = null               -- true if My_Car has been set to null (see 3.1\
0.1)
    My_Car = Your_Car           -- true if we both share the same car
    My_Car.all = Your_Car.all   -- true if the two cars are identical

39  N not in 1 .. 10            -- range membership test
    Today in Mon .. Fri         -- range membership test
    Today in Weekday            -- subtype membership test (see 3.5.1)
    Archive in Disk_Unit        -- subtype membership test (see 3.8.1)
    Tree.all in Addition'Class  -- class membership test (see 3.9.1)


                            Extensions to Ada 83

        39.a   {extensions to Ada 83} Membership tests can be used to test
        the tag of a class-wide value.

        39.b   Predefined equality for a composite type is defined in terms
        of the primitive equals operator for tagged components or the parent
        part.

                         Wording Changes From Ada 83

        39.c   The term ``membership test'' refers to the relation "X in S"
        rather to simply the reserved word in or not in.

        39.d   We use the term ``equality operator'' to refer to both the =
        (equals) and /= (not equals) operators.  Ada 83 referred to = as the
        equality operator, and /= as the inequality operator.  The new
        wording is more consistent with the ISO 10646 name for "=" (equals
        sign) and provides a category similar to ``ordering operator'' to
        refer to both = and /=.

        39.e   We have changed the term ``catenate'' to ``concatenate''.



4.5.3 Binary Adding Operators

                              Static Semantics

1   {binary adding operator} {operator (binary adding)} {+ operator}
{operator (+)} {plus operator} {operator (plus)} {- operator} {operator (-)}
{minus operator} {operator (minus)} The binary adding operators + (addition)
and - (subtraction) are predefined for every specific numeric type T with
their conventional meaning.  They have the following specifications:

2   function "+"(Left, Right : T) return T
    function "-"(Left, Right : T) return T

3   {& operator} {operator (&)} {ampersand operator} {operator (ampersand)}
{concatenation operator} {operator (concatenation)} {catenation operator: see
concatenation operator} The concatenation operators & are predefined for
every nonlimited, one-dimensional array type T with component type C.  They
have the following specifications:

4   function "&"(Left : T; Right : T) return T
    function "&"(Left : T; Right : C) return T
    function "&"(Left : C; Right : T) return T
    function "&"(Left : C; Right : C) return T


                              Dynamic Semantics

5   {evaluation [concatenation]} For the evaluation of a concatenation with
result type T, if both operands are of type T, the result of the
concatenation is a one-dimensional array whose length is the sum of the
lengths of its operands, and whose components comprise the components of the
left operand followed by the components of the right operand.  If the left
operand is a null array, the result of the concatenation is the right
operand.  Otherwise, the lower bound of the result is determined as follows:

    6  If the ultimate ancestor of the array type was defined by a
       constrained_array_definition, then the lower bound of the result
       is that of the index subtype;

 6.a    Reason:  This rule avoids Constraint_Error when using
        concatenation on an array type whose first subtype is
        constrained.

    7  If the ultimate ancestor of the array type was defined by an
       unconstrained_array_definition, then the lower bound of the
       result is that of the left operand.

8   [The upper bound is determined by the lower bound and the length.]
{Index_Check [partial]} {check, language-defined (Index_Check)} A check is
made that the upper bound of the result of the concatenation belongs to the
range of the index subtype, unless the result is a null array.  {Constraint_
Error (raised by failure of run-time check)} Constraint_Error is raised if
this check fails.

9   If either operand is of the component type C, the result of the
concatenation is given by the above rules, using in place of such an operand
an array having this operand as its only component (converted to the
component subtype) and having the lower bound of the index subtype of the
array type as its lower bound.  {implicit subtype conversion [operand of
concatenation]}
        9.a   Ramification:  The conversion might raise Constraint_Error.
        The conversion provides ``sliding'' for the component in the case of
        an array-of-arrays, consistent with the normal Ada 9X rules that
        allow sliding during parameter passing.

10   {assignment operation (during evaluation of concatenation)} The result
of a concatenation is defined in terms of an assignment to an anonymous
object, as for any function call (see 6.5).

        10.a   Ramification:  This implies that value adjustment is performed
        as appropriate -- see 7.6.  We don't bother saying this for other
        predefined operators, even though they are all function calls,
        because this is the only one where it matters.  It is the only one
        that can return a value having controlled parts.


     NOTES
11   (15) As for all predefined operators on modular types, the binary adding
     operators + and - on modular types include a final reduction modulo the
     modulus if the result is outside the base range of the type.

   11.a   Implementation Note:  A full "modulus" operation need not be
        performed after addition or subtraction of modular types.  For binary
        moduli, a simple mask is sufficient.  For nonbinary moduli, a check
        after addition to see if the value is greater than the high bound of
        the base range can be followed by a conditional subtraction of the
        modulus.  Conversely, a check after subtraction to see if a "borrow"
        was performed can be followed by a conditional addition of the
        modulus.


                                  Examples

12   Examples of expressions involving binary adding operators:

13  Z + 0.1      --  Z has to be of a real type

14  "A" & "BCD"  --  concatenation of two string literals
    'A' & "BCD"  --  concatenation of a character literal and a string literal
    'A' & 'A'    --  concatenation of two character literals


                         Inconsistencies With Ada 83

        14.a   {inconsistencies with Ada 83} The lower bound of the result of
        concatenation, for a type whose first subtype is constrained, is now
        that of the index subtype.  This is inconsistent with Ada 83, but
        generally only for Ada 83 programs that raise Constraint_Error.  For
        example, the concatenation operator in

14.b        X : array(1..10) of Integer;
            begin
            X := X(6..10) & X(1..5);

        14.c   would raise Constraint_Error in Ada 83 (because the bounds of
        the result of the concatenation would be 6..15, which is outside of
        1..10), but would succeed and swap the halves of X (as expected) in
        Ada 9X.

                            Extensions to Ada 83

        14.d   {extensions to Ada 83} Concatenation is now useful for array
        types whose first subtype is constrained.  When the result type of a
        concatenation is such an array type, Constraint_Error is avoided by
        effectively first sliding the left operand (if nonnull) so that its
        lower bound is that of the index subtype.



4.5.4 Unary Adding Operators

                              Static Semantics

1   {unary adding operator} {operator (unary adding)} {+ operator} {operator
(+)} {plus operator} {operator (plus)} {- operator} {operator (-)} {minus
operator} {operator (minus)} The unary adding operators + (identity) and -
(negation) are predefined for every specific numeric type T with their
conventional meaning.  They have the following specifications:

2   function "+"(Right : T) return T
    function "-"(Right : T) return T


     NOTES
3    (16) For modular integer types, the unary adding operator -, when given
     a nonzero operand, returns the result of subtracting the value of the
     operand from the modulus; for a zero operand, the result is zero.



4.5.5 Multiplying Operators

                              Static Semantics

1   {multiplying operator} {operator (multiplying)} {* operator} {operator
(*)} {multiply operator} {operator (multiply)} {times operator} {operator
(times)} {/ operator} {operator (/)} {divide operator} {operator (divide)}
{mod operator} {operator (mod)} {rem operator} {operator (rem)} The
multiplying operators * (multiplication), / (division), mod (modulus), and
rem (remainder) are predefined for every specific integer type T:

2   function "*"  (Left, Right : T) return T
    function "/"  (Left, Right : T) return T
    function "mod"(Left, Right : T) return T
    function "rem"(Left, Right : T) return T

3   Signed integer multiplication has its conventional meaning.

4   Signed integer division and remainder are defined by the relation:

5   A = (A/B)*B + (A rem B)

6   where (A rem B) has the sign of A and an absolute value less than the
absolute value of B. Signed integer division satisfies the identity:

7   (-A)/B = -(A/B) = A/(-B)

8   The signed integer modulus operator is defined such that the result of A
mod B has the sign of B and an absolute value less than the absolute value of
B; in addition, for some signed integer value N, this result satisfies the
relation:

9   A = B*N + (A mod B)

10   [The multiplying operators on modular types are defined in terms of the
corresponding signed integer operators, followed by a reduction modulo the
modulus if the result is outside the base range of the type [(which is only
possible for the "*" operator)].]

        10.a   Ramification:  The above identity satisfied by signed integer
        division is not satisfied by modular division because of the
        difference in effect of negation.

11   Multiplication and division operators are predefined for every specific
floating point type T:

12  function "*"(Left, Right : T) return T
    function "/"(Left, Right : T) return T

13   The following multiplication and division operators, with an operand of
the predefined type Integer, are predefined for every specific fixed point
type T:

14  function "*"(Left : T; Right : Integer) return T
    function "*"(Left : Integer; Right : T) return T
    function "/"(Left : T; Right : Integer) return T

15   [All of the above multiplying operators are usable with an operand of an
appropriate universal numeric type.]  The following additional multiplying
operators for root_real are predefined[, and are usable when both operands
are of an appropriate universal or root numeric type, and the result is
allowed to be of type root_real, as in a number_declaration]:

        15.a   Ramification:  These operators are analogous to the
        multiplying operators involving fixed or floating point types where
        root_real substitutes for the fixed or floating point type, and root_
        integer substitutes for Integer.  Only values of the corresponding
        universal numeric types are implicitly convertible to these root
        numeric types, so these operators are really restricted to use with
        operands of a universal type, or the specified root numeric types.

16  function "*"(Left, Right : root_real) return root_real
    function "/"(Left, Right : root_real) return root_real

17  function "*"(Left : root_real; Right : root_integer) return root_real
    function "*"(Left : root_integer; Right : root_real) return root_real
    function "/"(Left : root_real; Right : root_integer) return root_real

18   Multiplication and division between any two fixed point types are
provided by the following two predefined operators:

        18.a   Ramification:  Universal_fixed is the universal type for the
        class of fixed point types, meaning that these operators take
        operands of any fixed point types (not necessarily the same) and
        return a result that is implicitly (or explicitly) convertible to any
        fixed point type.

19  function "*"(Left, Right : universal_fixed) return universal_fixed
    function "/"(Left, Right : universal_fixed) return universal_fixed


                               Legality Rules

20   The above two fixed-fixed multiplying operators shall not be used in a
context where the expected type for the result is itself universal_fixed --
[the context has to identify some other numeric type to which the result is
to be converted, either explicitly or implicitly].

        20.a   Discussion:  The small of universal_fixed is infinitesimal; no
        loss of precision is permitted.  However, fixed-fixed division is
        impractical to implement when an exact result is required, and
        multiplication will sometimes result in unanticipated overflows in
        such circumstances, so we require an explicit conversion to be
        inserted in expressions like A * B * C if A, B, and C are each of
        some fixed point type.

        20.b   On the other hand, X := A * B; is permitted by this rule, even
        if X, A, and B are all of different fixed point types, since the
        expected type for the result of the multiplication is the type of X,
        which is necessarily not universal_fixed.
                              Dynamic Semantics

21   The multiplication and division operators for real types have their
conventional meaning.[For floating point types, the accuracy of the result is
determined by the precision of the result type.  For decimal fixed point
types, the result is truncated toward zero if the mathematical result is
between two multiples of the small of the specific result type (possibly
determined by context); for ordinary fixed point types, if the mathematical
result is between two multiples of the small, it is unspecified which of the
two is the result.  {unspecified [partial]}]

22   {Division_Check [partial]} {check, language-defined (Division_Check)}
{Constraint_Error (raised by failure of run-time check)} The exception
Constraint_Error is raised by integer division, rem, and mod if the right
operand is zero.  [Similarly, for a real type T with T'Machine_Overflows
True, division by zero raises Constraint_Error.]


     NOTES
23   (17) For positive A and B, A/B is the quotient and A rem B is the
     remainder when A is divided by B. The following relations are satisfied
     by the rem operator:

24         A  rem (-B) =   A rem B
         (-A) rem   B  = -(A rem B)

25   (18) For any signed integer K, the following identity holds:

26       A mod B   =   (A + K*B) mod B

27The relations between signed integer  division, remainder, and
     modulus are  illustrated by the following table:

28       A      B   A/B   A rem B  A mod B     A     B    A/B   A rem B   A mod\
 B

29       10     5    2       0        0       -10    5    -2       0         0
         11     5    2       1        1       -11    5    -2      -1         4
         12     5    2       2        2       -12    5    -2      -2         3
         13     5    2       3        3       -13    5    -2      -3         2
         14     5    2       4        4       -14    5    -2      -4         1

30       A      B   A/B   A rem B  A mod B     A     B    A/B   A rem B   A mod\
 B
         10    -5   -2       0        0       -10   -5     2       0         0
         11    -5   -2       1       -4       -11   -5     2      -1        -1
         12    -5   -2       2       -3       -12   -5     2      -2        -2
         13    -5   -2       3       -2       -13   -5     2      -3        -3
         14    -5   -2       4       -1       -14   -5     2      -4        -4


                                  Examples

31   Examples of expressions involving multiplying operators:

32  I : Integer := 1;
    J : Integer := 2;
    K : Integer := 3;

33  X : Real := 1.0;                      --     see 3.5.7
    Y : Real := 2.0;

34  F : Fraction := 0.25;                 --     see 3.5.9
    G : Fraction := 0.5;

35
    Expression                Value           Result Type

    I*J                       2               same as I and J, that is, Integer
    K/J                       1               same as K and J, that is, Integer
    K mod J                   1               same as K and J, that is, Integer

    X/Y                       0.5             same as X and Y, that is, Real
    F/2                       0.125           same as F, that is, Fraction

    3*F                       0.75            same as F, that is, Fraction
    0.75*G                    0.375           universal_fixed, implicitly conve\
rtible
                                              to any fixed point type
    Fraction(F*G)             0.125           Fraction, as stated by the conver\
sion
    Real(J)*Y                 4.0             Real, the type of both operands a\
fter
                                              conversion of J


                            Extensions to Ada 83

        35.a   {extensions to Ada 83} Explicit conversion of the result of
        multiplying or dividing two fixed point numbers is no longer
        required, provided the context uniquely determines some specific
        fixed point result type.  This is to improve support for decimal
        fixed point, where requiring explicit conversion on every fixed-fixed
        multiply or divide was felt to be inappropriate.

        35.b   The type universal_fixed is covered by universal_real, so real
        literals and fixed point operands may be multiplied or divided
        directly, without any explicit conversions required.

                         Wording Changes From Ada 83

        35.c   We have used the normal syntax for function definition rather
        than a tabular format.



4.5.6 Highest Precedence Operators

                              Static Semantics

1   {highest precedence operator} {operator (highest precedence)} {abs
operator} {operator (abs)} {absolute value} The highest precedence unary
operator abs (absolute value) is predefined for every specific numeric type
T, with the following specification:

2   function "abs"(Right : T) return T

3   {not operator} {operator (not)} {logical operator: see also not operator}
The highest precedence unary operator not (logical negation) is predefined
for every boolean type T, every modular type T, and for every one-dimensional
array type T whose components are of a boolean type, with the following
specification:

4   function "not"(Right : T) return T

5   The result of the operator not for a modular type is defined as the
difference between the high bound of the base range of the type and the value
of the operand.  [For a binary modulus, this corresponds to a bit-wise
complement of the binary representation of the value of the operand.]

6   The operator not that applies to a one-dimensional array of boolean
components yields a one-dimensional boolean array with the same bounds; each
component of the result is obtained by logical negation of the corresponding
component of the operand (that is, the component that has the same index
value).  {Range_Check [partial]} {check, language-defined (Range_Check)}
{Constraint_Error (raised by failure of run-time check)} A check is made that
each component of the result belongs to the component subtype; the exception
Constraint_Error is raised if this check fails.

        6.a   Discussion:  The check against the component subtype is per
        AI-00535.

7   {exponentiation operator} {operator (exponentiation)} {** operator}
{operator (**)} The highest precedence exponentiation operator ** is
predefined for every specific integer type T with the following
specification:  {94-4693.v}

8   function "**"(Left : T; Right : Natural) return T

9   Exponentiation is also predefined for every specific floating point type
as well as root_real, with the following specification (where T is root_real
or the floating point type):

10  function "**"(Left : T; Right : Integer'Base) return T

11   {exponent} The right operand of an exponentiation is the exponent.  The
expression X**N with the value of the exponent N positive is equivalent to
the expression X*X*...X (with N-1 multiplications) except that the
multiplications are associated in an arbitrary order.  With N equal to zero,
the result is one.  With the value of N negative [(only defined for a
floating point operand)], the result is the reciprocal of the result using
the absolute value of N as the exponent.

        11.a   Ramification:  The language does not specify the order of
        association of the multiplications inherent in an exponentiation.
        For a floating point type, the accuracy of the result might depend on
        the particular association order chosen.


                         Implementation Permissions

12   {Constraint_Error (raised by failure of run-time check)} The
implementation of exponentiation for the case of a negative exponent is
allowed to raise Constraint_Error if the intermediate result of the repeated
multiplications is outside the safe range of the type, even though the final
result (after taking the reciprocal) would not be.  (The best machine
approximation to the final result in this case would generally be 0.0.)


     NOTES
13   (19) {Range_Check [partial]} {check, language-defined (Range_Check)} As
     implied by the specification given above for exponentiation of an
     integer type, a check is made that the exponent is not negative.
     {Constraint_Error (raised by failure of run-time check)} Constraint_
     Error is raised if this check fails.


                         Wording Changes From Ada 83

        13.a   We now show the specification for "**" for integer types with
        a parameter subtype of Natural rather than Integer for the exponent.
        This reflects the fact that Constraint_Error is raised if a negative
        value is provided for the exponent.



4.6 Type Conversions

1   [Explicit type conversions, both value conversions and view conversions,
are allowed between closely related types as defined below.  This clause also
defines rules for value and view conversions to a particular subtype of a
type, both explicit ones and those implicit in other constructs.  {subtype
conversion: see type conversion} {type conversion} {conversion} {cast: see
type conversion} ]{subtype conversion: see also implicit subtype conversion}
{type conversion, implicit: see implicit subtype conversion}
                                   Syntax

2   type_conversion ::=
        subtype_mark(expression)
      | subtype_mark(name)


3   {target subtype (of a type_conversion)} The target subtype of a type_
conversion is the subtype denoted by the subtype_mark.  {operand (of a type_
conversion)} The operand of a type_conversion is the expression or name
within the parentheses; {operand type (of a type_conversion)} its type is the
operand type.

4   {convertible} One type is convertible to a second type if a type_
conversion with the first type as operand type and the second type as target
type is legal according to the rules of this clause.  Two types are
convertible if each is convertible to the other.

        4.a   Ramification:  Note that ``convertible'' is defined in terms of
        legality of the conversion.  Whether the conversion would raise an
        exception at run time is irrelevant to this definition.

5   {view conversion} {conversion (view)} A type_conversion whose operand is
the name of an object is called a view conversion if its target type is
tagged, or if it appears as an actual parameter of mode out or in out; {value
conversion} {conversion (value)} other type_conversions are called value
conversions.  {super: see view conversion}

        5.a   Ramification:  A view conversion to a tagged type can appear in
        any context that requires an object name, including in an object
        renaming, the prefix of a selected_component, and if the operand is a
        variable, on the left side of an assignment_statement.  View
        conversions to other types only occur as actual parameters.  Allowing
        view conversions of untagged types in all contexts seemed to incur an
        undue implementation burden.


                            Name Resolution Rules

6   {expected type [type_conversion operand]} The operand of a type_
conversion is expected to be of any type.

        6.a   Discussion:  This replaces the "must be determinable" wording
        of Ada 83.  This is equivalent to (but hopefully more intuitive than)
        saying that the operand of a type_conversion is a ``complete
        context.''

7   The operand of a view conversion is interpreted only as a name; the
operand of a value conversion is interpreted as an expression.

        7.a   Reason:  This formally resolves the syntactic ambiguity between
        the two forms of type_conversion, not that it really matters.


                               Legality Rules

8   {type conversion (numeric)} {conversion (numeric)} If the target type is
a numeric type, then the operand type shall be a numeric type.

9   {type conversion (array)} {conversion (array)} If the target type is an
array type, then the operand type shall be an array type.  Further:

   10  The types shall have the same dimensionality;

   11  Corresponding index types shall be convertible; and {convertible
       [required]}

   12  The component subtypes shall statically match.  {statically
       matching [required]}

13   {type conversion (access)} {conversion (access)} If the target type is a
general access type, then the operand type shall be an access-to-object type.
Further:

        13.a   Discussion:  The Legality Rules and Dynamic Semantics are
        worded so that a type_conversion T(X) (where T is an access type) is
        (almost) equivalent to the attribute_reference X.all'Access, where
        the result is of type T. The type_conversion accepts a null value,
        whereas the attribute_reference would raise Constraint_Error.

   14  If the target type is an access-to-variable type, then the
       operand type shall be an access-to-variable type;

 14.a   Ramification:  If the target type is an access-to-constant type,
        then the operand type can be access-to-constant or
        access-to-variable.

   15  If the target designated type is tagged, then the operand
       designated type shall be convertible to the target designated
       type; {convertible [required]}

   16  If the target designated type is not tagged, then the designated
       types shall be the same, and either the designated subtypes shall
       statically match or the target designated subtype shall be
       discriminated and unconstrained; and {statically matching
       [required]}

 16.a   Reason:  These rules are designed to ensure that aliased array
        objects only need "dope" if their nominal subtype is
        unconstrained, but they can always have dope if required by the
        run-time model (since no sliding is permitted as part of access
        type conversion).  By contrast, aliased discriminated objects
        will always need their discriminants stored with them, even if
        nominally constrained.  (Here, we are assuming an implementation
        that represents an access value as a single pointer.)

   17  {accessibility rule [type conversion]} The accessibility level of
       the operand type shall not be statically deeper than that of the
       target type.  {94-4715.a} {generic contract issue [partial]} In
       addition to the places where Legality Rules normally apply (see
       12.3), this rule applies also in the private part of an instance
       of a generic unit.

 17.a   Ramification:  The access parameter case is handled by a
        run-time check.  Run-time checks are also done in instance
        bodies.

18   {type conversion (access)} {conversion (access)} If the target type is
an access-to-subprogram type, then the operand type shall be an
access-to-subprogram type.  Further:

   19  The designated profiles shall be subtype-conformant.  {subtype
       conformance (required)}

   20  {accessibility rule [type conversion]} The accessibility level of
       the operand type shall not be statically deeper than that of the
       target type.  {94-4715.a} {generic contract issue [partial]} In
       addition to the places where Legality Rules normally apply (see
       12.3), this rule applies also in the private part of an instance
       of a generic unit.  If the operand type is declared within a
       generic body, the target type shall be declared within the
       generic body.  {94-4692.a} {94-4702.a} {94-4706.a} {94-4708.a}

 20.a   Reason:  The reason it is illegal to convert from an
        access-to-subprogram type declared in a generic body to one
        declared outside that body is that in an implementation that
        shares generic bodies, procedures declared inside the generic
        need to have a different calling convention -- they need an
        extra parameter pointing to the data declared in the current
        instance.  For procedures declared in the spec, that's OK,
        because the compiler can know about them at compile time of the
        instantiation.

21   {type conversion (enumeration)} {conversion (enumeration)} {type
conversion (composite (non-array))} {conversion (composite (non-array))} If
the target type is not included in any of the above four cases, there shall
be a type that is an ancestor of both the target type and the operand type.
Further, if the target type is tagged, then either:

   22  The operand type shall be covered by or descended from the target
       type; or

 22.a   Ramification:  This is a conversion toward the root, which is
        always safe.

   23  The operand type shall be a class-wide type that covers the
       target type.

 23.a   Ramification:  This is a conversion of a class-wide type toward
        the leaves, which requires a tag check.  See Dynamic Semantics.

 23.b   These two rules imply that a conversion from a parent type to a
        type extension is not permitted, as this would require
        specifying the values for additional components, in general, and
        changing the tag.  An extension_aggregate has to be used
        instead, constructing a new value, rather than converting an
        existing value.  However, a conversion from the class-wide type
        rooted at the parent type is permitted; such a conversion just
        verifies that the operand's tag is a descendant of the target.

24   In a view conversion for an untagged type, the target type shall be
convertible (back) to the operand type.

        24.a   Reason:  Untagged view conversions appear only as [in] out
        parameters.  Hence, the reverse conversion must be legal as well.
        The forward conversion must be legal even if an out parameter,
        because actual parameters of an access type are always copied in
        anyway.


                              Static Semantics

25   A type_conversion that is a value conversion denotes the value that is
the result of converting the value of the operand to the target subtype.

26   A type_conversion that is a view conversion denotes a view of the object
denoted by the operand.  This view is a variable of the target type if the
operand denotes a variable; otherwise it is a constant of the target type.

27   {nominal subtype [associated with a type_conversion]} The nominal
subtype of a type_conversion is its target subtype.


                              Dynamic Semantics

28   {evaluation [value conversion]} {corresponding value (of the target type
of a conversion)} {conversion} For the evaluation of a type_conversion that
is a value conversion, the operand is evaluated, and then the value of the
operand is converted to a corresponding value of the target type, if any.
{Range_Check [partial]} {check, language-defined (Range_Check)} {Constraint_
Error (raised by failure of run-time check)} If there is no value of the
target type that corresponds to the operand value, Constraint_Error is
raised[; this can only happen on conversion to a modular type, and only when
the operand value is outside the base range of the modular type.]  Additional
rules follow:  {94-4667.l}

   29  {type conversion (numeric)} {conversion (numeric)} Numeric Type
       Conversion

          30  If the target and the operand types are both integer
              types, then the result is the value of the target type
              that corresponds to the same mathematical integer as the
              operand.

          31  If the target type is a decimal fixed point type, then the
              result is truncated (toward 0) if the value of the operand
              is not a multiple of the small of the target type.

          32  {accuracy} If the target type is some other real type,
              then the result is within the accuracy of the target type
              (see G.2, ``Numeric Performance Requirements'', for
              implementations that support the Numerics Annex).
              {94-4481.a}

 32.a   Discussion:  An integer type might have more bits of precision
        than a real type, so on conversion (of a large integer), some
        precision might be lost.

          33  If the target type is an integer type and the operand type
              is real, the result is rounded to the nearest integer
              (away from zero if exactly halfway between two integers).

 33.a   Discussion:  This was implementation defined in Ada 83.  There
        seems no reason to preserve the nonportability in Ada 9X.
        Round-away-from-zero is the conventional definition of rounding,
        and standard Fortran and COBOL both specify rounding away from
        zero, so for interoperability, it seems important to pick this.
        This is also the most easily ``undone'' by hand.
        Round-to-nearest-even is an alternative, but that is quite
        complicated if not supported by the hardware.  In any case, this
        operation is not expected to be part of an inner loop, so
        predictability and portability are judged most important.  We
        anticipate that a floating point attribute function Unbiased_
        Rounding will be provided for those applications that require
        round-to-nearest-even.  ``Deterministic'' rounding is required
        for static conversions to integer as well.  See 4.9.

   34  {type conversion (enumeration)} {conversion (enumeration)}
       Enumeration Type Conversion

          35  The result is the value of the target type with the same
              position number as that of the operand value.

   36  {type conversion (array)} {conversion (array)} Array Type
       Conversion

          37  {Length_Check [partial]} {check, language-defined (Length_
              Check)} If the target subtype is a constrained array
              subtype, then a check is made that the length of each
              dimension of the value of the operand equals the length of
              the corresponding dimension of the target subtype.  The
              bounds of the result are those of the target subtype.

          38  {Range_Check [partial]} {check, language-defined (Range_
              Check)} If the target subtype is an unconstrained array
              subtype, then the bounds of the result are obtained by
              converting each bound of the value of the operand to the
              corresponding index type of the target type.  {implicit
              subtype conversion [array bounds]} For each nonnull index
              range, a check is made that the bounds of the range belong
              to the corresponding index subtype.

 38.a   Discussion:  Only nonnull index ranges are checked, per
        AI-00313.

          39  In either array case, the value of each component of the
              result is that of the matching component of the operand
              value (see 4.5.2).

 39.a   Ramification:  This applies whether or not the component is
        initialized.

   40  {type conversion (composite (non-array))} {conversion (composite
       (non-array))} Composite (Non-Array) Type Conversion

          41  The value of each nondiscriminant component of the result
              is that of the matching component of the operand value.

 41.a   Ramification:  This applies whether or not the component is
        initialized.

          42  [The tag of the result is that of the operand.]  {Tag_
              Check [partial]} {check, language-defined (Tag_Check)} If
              the operand type is class-wide, a check is made that the
              tag of the operand identifies a (specific) type that is
              covered by or descended from the target type.

 42.a   Ramification:  This check is certain to succeed if the operand
        type is itself covered by or descended from the target type.

 42.b   Proof:  The fact that a type_conversion preserves the tag is
        stated officially in 3.9, ``Tagged Types and Type Extensions''

          43  For each discriminant of the target type that corresponds
              to a discriminant of the operand type, its value is that
              of the corresponding discriminant of the operand value;
              {Discriminant_Check [partial]} {check, language-defined
              (Discriminant_Check)} if it corresponds to more than one
              discriminant of the operand type, a check is made that all
              these discriminants are equal in the operand value.

          44  For each discriminant of the target type that corresponds
              to a discriminant that is specified by the derived_type_
              definition for some ancestor of the operand type (or if
              class-wide, some ancestor of the specific type identified
              by the tag of the operand), its value in the result is
              that specified by the derived_type_definition.

 44.a   Ramification:  It is a ramification of the rules for the
        discriminants of derived types that each discriminant of the
        result is covered either by this paragraph or the previous one.
        See 3.7.

          45  {Discriminant_Check [partial]} {check, language-defined
              (Discriminant_Check)} For each discriminant of the operand
              type that corresponds to a discriminant that is specified
              by the derived_type_definition for some ancestor of the
              target type, a check is made that in the operand value it
              equals the value specified for it.

          46  {Range_Check [partial]} {check, language-defined (Range_
              Check)} For each discriminant of the result, a check is
              made that its value belongs to its subtype.

   47  {type conversion (access)} {conversion (access)} Access Type
       Conversion

          48  {Accessibility_Check [partial]} {check, language-defined
              (Accessibility_Check)} For an access-to-object type, a
              check is made that the accessibility level of the operand
              type is not deeper than that of the target type.
              {94-4715.a}

 48.a   Ramification:  This check is needed for operands that are access
        parameters and in instance bodies.

 48.b   Note that this check can never fail for the implicit conversion
        to the anonymous type of an access parameter that is done when
        calling a subprogram with an access parameter.  {94-4715.a}

          49  {Access_Check [partial]} {check, language-defined (Access_
              Check)} If the target type is an anonymous access type, a
              check is made that the value of the operand is not null;
              if the target is not an anonymous access type, then the
              result is null if the operand value is null.

 49.a   Ramification:  A conversion to an anonymous access type happens
        implicitly as part of initializing an access discriminant or
        access parameter.

 49.b   Reason:  As explained in 3.10, ``Access Types'', it is important
        that a value of an anonymous access type can never be null.

          50  If the operand value is not null, then the result
              designates the same object (or subprogram) as is
              designated by the operand value, but viewed as being of
              the target designated subtype (or profile); any checks
              associated with evaluating a conversion to the target
              designated subtype are performed.

 50.a   Ramification:  The checks are certain to succeed if the target
        and operand designated subtypes statically match.

51   {Range_Check [partial]} {check, language-defined (Range_Check)}
{Discriminant_Check [partial]} {check, language-defined (Discriminant_Check)}
{Index_Check [partial]} {check, language-defined (Index_Check)} After
conversion of the value to the target type, if the target subtype is
constrained, a check is performed that the value satisfies this constraint.

        51.a   Ramification:  The above check is a Range_Check for scalar
        subtypes, a Discriminant_Check or Index_Check for access subtypes,
        and a Discriminant_Check for discriminated subtypes.  The Length_
        Check for an array conversion is performed as part of the conversion
        to the target type.

52   {evaluation [view conversion]} For the evaluation of a view conversion,
the operand name is evaluated, and a new view of the object denoted by the
operand is created, whose type is the target type; {Length_Check [partial]}
{check, language-defined (Length_Check)} {Tag_Check [partial]} {check,
language-defined (Tag_Check)} {Discriminant_Check [partial]} {check,
language-defined (Discriminant_Check)} if the target type is composite,
checks are performed as above for a value conversion.

53   The properties of this new view are as follows:

   54  If the target type is composite, the bounds or discriminants (if
       any) of the view are as defined above for a value conversion;
       each nondiscriminant component of the view denotes the matching
       component of the operand object; the subtype of the view is
       constrained if either the target subtype or the operand object is
       constrained, or if the operand type is a descendant of the target
       type, and has discriminants that were not inherited from the
       target type;

   55  If the target type is tagged, then an assignment to the view
       assigns to the corresponding part of the object denoted by the
       operand; otherwise, an assignment to the view assigns to the
       object, after converting the assigned value to the subtype of the
       object (which might raise Constraint_Error); {implicit subtype
       conversion [assignment to view conversion]}

   56  Reading the value of the view yields the result of converting the
       value of the operand object to the target subtype (which might
       raise Constraint_Error), except if the object is of an access
       type and the view conversion is passed as an out parameter; in
       this latter case, the value of the operand object is used to
       initialize the formal parameter without checking against any
       constraint of the target subtype (see 6.4.1).  {implicit subtype
       conversion [reading a view conversion]}

 56.a   Reason:  This ensures that even an out parameter of an access
        type is initialized reasonably.

57   {Program_Error (raised by failure of run-time check)} {Constraint_Error
(raised by failure of run-time check)} If an Accessibility_Check fails,
Program_Error is raised.  Any other check associated with a conversion raises
Constraint_Error if it fails.

58   Conversion to a type is the same as conversion to an unconstrained
subtype of the type.

        58.a   Reason:  This definition is needed because the semantics of
        various constructs involves converting to a type, whereas an explicit
        type_conversion actually converts to a subtype.  For example, the
        evaluation of a range is defined to convert the values of the
        expressions to the type of the range.

        58.b   Ramification:  A conversion to a scalar type, or,
        equivalently, to an unconstrained scalar subtype, can raise
        Constraint_Error if the value is outside the base range of the type.


     NOTES
59   (20) {implicit subtype conversion [distributed]} In addition to explicit
     type_conversions, type conversions are performed implicitly in
     situations where the expected type and the actual type of a construct
     differ, as is permitted by the type resolution rules (see 8.6).  For
     example, an integer literal is of the type universal_integer, and is
     implicitly converted when assigned to a target of some specific integer
     type.  Similarly, an actual parameter of a specific tagged type is
     implicitly converted when the corresponding formal parameter is of a
     class-wide type.

     60   {implicit subtype conversion [distributed]} {Constraint_Error
     (raised by failure of run-time check)} Even when the expected and actual
     types are the same, implicit subtype conversions are performed to adjust
     the array bounds (if any) of an operand to match the desired target
     subtype, or to raise Constraint_Error if the (possibly adjusted) value
     does not satisfy the constraints of the target subtype.

61   (21) A ramification of the overload resolution rules is that the operand
     of an (explicit) type_conversion cannot be the literal null, an
     allocator, an aggregate, a string_literal, a character_literal, or an
     attribute_reference for an Access or Unchecked_Access attribute.
     Similarly, such an expression enclosed by parentheses is not allowed.  A
     qualified_expression (see 4.7) can be used instead of such a type_
     conversion.

62   (22) The constraint of the target subtype has no effect for a type_
     conversion of an elementary type passed as an out parameter.  Hence, it
     is recommended that the first subtype be specified as the target to
     minimize confusion (a similar recommendation applies to renaming and
     generic formal in out objects).


                                  Examples

63   Examples of numeric type conversion:

64  Real(2*J)      --  value is converted to floating point
    Integer(1.6)   --  value is 2
    Integer(-0.4)  --  value is 0

65   Example of conversion between derived types:

66  type A_Form is new B_Form;

67  X : A_Form;
    Y : B_Form;

68  X := A_Form(Y);
    Y := B_Form(X);  --  the reverse conversion

69   Examples of conversions between array types:

70  type Sequence is array (Integer range <>) of Integer;
    subtype Dozen is Sequence(1 .. 12);
    Ledger : array(1 .. 100) of Integer;

71  Sequence(Ledger)            --  bounds are those of Ledger
    Sequence(Ledger(31 .. 42))  --  bounds are 31 and 42
    Dozen(Ledger(31 .. 42))     --  bounds are those of Dozen


                        Incompatibilities With Ada 83

        71.a   {incompatibilities with Ada 83} A character_literal is not
        allowed as the operand of a type_conversion, since there are now two
        character types in package Standard.

        71.b   The component subtypes have to statically match in an array
        conversion, rather than being checked for matching constraints at run
        time.

        71.c   Because sliding of array bounds is now provided for operations
        where it was not in Ada 83, programs that used to raise Constraint_
        Error might now continue executing and produce a reasonable result.
        This is likely to fix more bugs than it creates.

                            Extensions to Ada 83

        71.d   {extensions to Ada 83} A type_conversion is considered the
        name of an object in certain circumstances (such a type_conversion is
        called a view conversion).  In particular, as in Ada 83, a type_
        conversion can appear as an in out or out actual parameter.  In
        addition, if the target type is tagged and the operand is the name of
        an object, then so is the type_conversion, and it can be used as the
        prefix to a selected_component, in an object_renaming_declaration,
        etc.

        71.e   We no longer require type-mark conformance between a parameter
        of the form of a type conversion, and the corresponding formal
        parameter.  This had caused some problems for inherited subprograms
        (since there isn't really a type-mark for converted formals), as well
        as for renamings, formal subprograms, etc.  See AI-245, AI-318,
        AI-547.

        71.f   We now specify ``deterministic'' rounding from real to integer
        types when the value of the operand is exactly between two integers
        (rounding is away from zero in this case).

        71.g   ``Sliding'' of array bounds (which is part of conversion to an
        array subtype) is performed in more cases in Ada 9X than in Ada 83.
        Sliding is not performed on the operand of a membership test, nor on
        the operand of a qualified_expression.  It wouldn't make sense on a
        membership test, and we wish to retain a connection between subtype
        membership and subtype qualification.  In general, a subtype
        membership test returns True if and only if a corresponding subtype
        qualification succeeds without raising an exception.  Other
        operations that take arrays perform sliding.

                         Wording Changes From Ada 83

        71.h   We no longer explicitly list the kinds of things that are not
        allowed as the operand of a type_conversion, except in a NOTE.

        71.i   The rules in this clause subsume the rules for "parameters of
        the form of a type conversion," and have been generalized to cover
        the use of a type conversion as a name.



4.7 Qualified Expressions

1   [A qualified_expression is used to state explicitly the type, and to
verify the subtype, of an operand that is either an expression or an
aggregate.  {type conversion: see also qualified_expression} ]


                                   Syntax

2   qualified_expression ::=
       subtype_mark'(expression) | subtype_mark'aggregate


                            Name Resolution Rules

3   {operand [of a qualified_expression]} The operand (the expression or
aggregate) shall resolve to be of the type determined by the subtype_mark, or
a universal type that covers it.


                              Dynamic Semantics

4   {evaluation [qualified_expression]} {Range_Check [partial]} {check,
language-defined (Range_Check)} {Discriminant_Check [partial]} {check,
language-defined (Discriminant_Check)} {Index_Check [partial]} {check,
language-defined (Index_Check)} The evaluation of a qualified_expression
evaluates the operand (and if of a universal type, converts it to the type
determined by the subtype_mark) and checks that its value belongs to the
subtype denoted by the subtype_mark.  {implicit subtype conversion
[qualified_expression]} {Constraint_Error (raised by failure of run-time
check)} The exception Constraint_Error is raised if this check fails.

        4.a   Ramification:  This is one of the few contexts in Ada 9X where
        implicit subtype conversion is not performed prior to a constraint
        check, and hence no ``sliding'' of array bounds is provided.

        4.b   Reason:  Implicit subtype conversion is not provided because a
        qualified_expression with a constrained target subtype is essentially
        an assertion about the subtype of the operand, rather than a request
        for conversion.  An explicit type_conversion can be used rather than
        a qualified_expression if subtype conversion is desired.


     NOTES
5    (23) When a given context does not uniquely identify an expected type, a
     qualified_expression can be used to do so.  In particular, if an
     overloaded name or aggregate is passed to an overloaded subprogram, it
     might be necessary to qualify the operand to resolve its type.


                                  Examples

6   Examples of disambiguating expressions using qualification:

7   type Mask is (Fix, Dec, Exp, Signif);
    type Code is (Fix, Cla, Dec, Tnz, Sub);

8   Print (Mask'(Dec));  --  Dec is of type Mask
    Print (Code'(Dec));  --  Dec is of type Code

9   for J in Code'(Fix) .. Code'(Dec) loop ... -- qualification needed for eith\
er Fix or Dec
    for J in Code range Fix .. Dec loop ...    -- qualification unnecessary
    for J in Code'(Fix) .. Dec loop ...        -- qualification unnecessary for\
 Dec

10  Dozen'(1 | 3 | 5 | 7 => 2, others => 0) -- see 4.6



4.8 Allocators

1   [The evaluation of an allocator creates an object and yields an access
value that designates the object.  {new: see allocator} {malloc: see
allocator} {heap management: see also alligator} ]


                                   Syntax

2   allocator ::=
       new subtype_indication | new qualified_expression


                            Name Resolution Rules

3   {expected type [allocator]} The expected type for an allocator shall be a
single access-to-object type whose designated type covers the type determined
by the subtype_mark of the subtype_indication or qualified_expression.

        3.a   Discussion:  See 8.6, ``The Context of Overload Resolution''
        for the meaning of ``shall be a single ... type whose ...''


                               Legality Rules

4   {initialized allocator} An initialized allocator is an allocator with a
qualified_expression.  {uninitialized allocator} An uninitialized allocator
is one with a subtype_indication.  In the subtype_indication of an
uninitialized allocator, a constraint is permitted only if the subtype_mark
denotes an [unconstrained] composite subtype; if there is no constraint, then
the subtype_mark shall denote a definite subtype.  {94-4759.a} {constructor:
see initialized alligator}

        4.a   Ramification:  For example, ... new S'Class ... (with no
        initialization expression) is illegal, but ... new S'Class'(X) ... is
        legal, and takes its tag and constraints from the initial value
        X. (Note that the former case cannot have a constraint.)

5   If the type of the allocator is an access-to-constant type, the allocator
shall be an initialized allocator.  If the designated type is limited, the
allocator shall be an uninitialized allocator.

        5.a   Ramification:  For an access-to-constant type whose designated
        type is limited, allocators are illegal.  The Access attribute is
        legal for such a type, however.


                              Static Semantics

6   If the designated type of the type of the allocator is elementary, then
the subtype of the created object is the designated subtype.  If the
designated type is composite, then the created object is always constrained;
if the designated subtype is constrained, then it provides the constraint of
the created object; otherwise, the object is constrained by its initial value
[(even if the designated subtype is unconstrained with defaults)].
{constrained by its initial value [partial]}

        6.a   Discussion:  See AI-00331.

        6.b   Reason:  All objects created by an allocator are aliased, and
        all aliased composite objects need to be constrained so that access
        subtypes work reasonably.


                              Dynamic Semantics

7   {evaluation [allocator]} For the evaluation of an allocator, the
elaboration of the subtype_indication or the evaluation of the qualified_
expression is performed first.  {evaluation [initialized allocator]}
{assignment operation (during evaluation of an initialized allocator)} For
the evaluation of an initialized allocator, an object of the designated type
is created and the value of the qualified_expression is converted to the
designated subtype and assigned to the object.  {implicit subtype conversion
[initialization expression of allocator]}

        7.a   Ramification:  The conversion might raise Constraint_Error.

8   {evaluation [uninitialized allocator]} For the evaluation of an
uninitialized allocator:

    9  {assignment operation (during evaluation of an uninitialized
       allocator)} If the designated type is elementary, an object of
       the designated subtype is created and any implicit initial value
       is assigned;

   10  {assignment operation (during evaluation of an uninitialized
       allocator)} If the designated type is composite, an object of the
       designated type is created with tag, if any, determined by the
       subtype_mark of the subtype_indication; any per-object con-
       straints on subcomponents are elaborated and any implicit initial
       values for the subcomponents of the object are obtained as
       determined by the subtype_indication and assigned to the
       corresponding subcomponents.  {Index_Check [partial]} {check,
       language-defined (Index_Check)} {Discriminant_Check [partial]}
       {check, language-defined (Discriminant_Check)} A check is made
       that the value of the object belongs to the designated subtype.
       {Constraint_Error (raised by failure of run-time check)}
       Constraint_Error is raised if this check fails.  This check and
       the initialization of the object are performed in an arbitrary
       order.

 10.a   Discussion:  AI-00150.

11   [If the created object contains any tasks, they are activated (see
9.2).]  Finally, an access value that designates the created object is
returned.


     NOTES
12   (24) Allocators cannot create objects of an abstract type.  See 3.9.3.

13   (25) If any part of the created object is controlled, the initialization
     includes calls on corresponding Initialize or Adjust procedures.  See
     7.6.

14   (26) As explained in 13.11, ``Storage Management'', the storage for an
     object allocated by an allocator comes from a storage pool (possibly
     user defined).  {Storage_Error (raised by failure of run-time check)}
     The exception Storage_Error is raised by an allocator if there is not
     enough storage.  Instances of Unchecked_Deallocation may be used to
     explicitly reclaim storage.

15   (27) Implementations are permitted, but not required, to provide garbage
     collection (see 13.11.3).

   15.a   Ramification:  Note that in an allocator, the exception Constraint_
        Error can be raised by the evaluation of the qualified_expression, by
        the elaboration of the subtype_indication, or by the initialization.

   15.b   Discussion:  By default, the implementation provides the storage
        pool.  The user may exercise more control over storage management by
        associating a user-defined pool with an access type.


                                  Examples

16   Examples of allocators:

17  new Cell'(0, null, null)                          -- initialized explicitly\
, see 3.10.1
    new Cell'(Value => 0, Succ => null, Pred => null) -- initialized explicitly
    new Cell                                          -- not initialized

18  new Matrix(1 .. 10, 1 .. 20)                      -- the bounds only are gi\
ven
    new Matrix'(1 .. 10 => (1 .. 20 => 0.0))          -- initialized explicitly

19  new Buffer(100)                                   -- the discriminant only \
is given
    new Buffer'(Size => 80, Pos => 0, Value => (1 .. 80 => 'A')) -- initialized\
 explicitly

20  Expr_Ptr'(new Literal)                        -- allocator for access-to-cl\
ass-wide type, see 3.9.1
    Expr_Ptr'(new Literal'(Expression with 3.5)) -- initialized explicitly


                        Incompatibilities With Ada 83

        20.a   {incompatibilities with Ada 83} The subtype_indication of an
        uninitialized allocator may not have an explicit constraint if the
        designated type is an access type.  In Ada 83, this was permitted
        even though the constraint had no affect on the subtype of the
        created object.

                            Extensions to Ada 83

        20.b   {extensions to Ada 83} Allocators creating objects of type T
        are now overloaded on access types designating T'Class and all
        class-wide types that cover T.

        20.c   Implicit array subtype conversion (sliding) is now performed
        as part of an initialized allocator.
                         Wording Changes From Ada 83

        20.d   We have used a new organization, inspired by the ACID
        document, that makes it clearer what is the subtype of the created
        object, and what subtype conversions take place.

        20.e   Discussion of storage management issues, such as garbage
        collection and the raising of Storage_Error, has been moved to 13.11,
        ``Storage Management''.



4.9 Static Expressions and Static Subtypes

1   Certain expressions of a scalar or string type are defined to be static.
Similarly, certain discrete ranges are defined to be static, and certain
scalar and string subtypes are defined to be static subtypes.  [{static}
Static means determinable at compile time, using the declared properties or
values of the program entities.]  {constant: see also static}

        1.a   Discussion:  As opposed to more elaborate data flow analysis,
        etc.


                         Language Design Principles

        1.b   For an expression to be static, it has to be calculable at
        compile time.

        1.c   Only scalar and string expressions are static.

        1.d   To be static, an expression cannot have any nonscalar,
        nonstring subexpressions (though it can have nonscalar constituent
        names).  A static scalar expression cannot have any nonscalar
        subexpressions.  There is one exception -- a membership test for a
        string subtype can be static, and the result is scalar, even though a
        subexpression is nonscalar.  {94-4679.a} {94-4684.a} {94-4687.a}

        1.e   The rules for evaluating static expressions are designed to
        maximize portability of static calculations.
2   {static (expression)} A static expression is [a scalar or string
expression that is] one of the following:  {94-4679.a} {94-4684.a}
{94-4687.a} {94-4738.a} {94-4926.a} {94-4929.a} {94-4950.a}

    3  a numeric_literal;

 3.a    Ramification:  A numeric_literal is always a static expression,
        even if its expected type is not that of a static subtype.
        However, if its value is explicitly converted to, or qualified
        by, a nonstatic subtype, the resulting expression is nonstatic.

    4  a string_literal of a static string subtype;

 4.a    Ramification:  That is, the constrained subtype defined by the
        index range of the string is static.  Note that elementary
        values don't generally have subtypes, while composite values do
        (since the bounds or discriminants are inherent in the value).

    5  a name that denotes the declaration of a named number or a static
       constant;

 5.a    Ramification:  Note that enumeration literals are covered by the
        function_call case.

    6  a function_call whose function_name or function_prefix statically
       denotes a static function, and whose actual parameters, if any
       (whether given explicitly or by default), are all static
       expressions;

 6.a    Ramification:  This includes uses of operators that are
        equivalent to function_calls.

    7  an attribute_reference that denotes a scalar value, and whose
       prefix denotes a static scalar subtype; {94-4679.c} {94-4684.c}

 7.a    Ramification:  Note that this does not include the case of an
        attribute that is a function; a reference to such an attribute
        is not even an expression.  See above for function calls.

 7.b    An implementation may define the staticness and other properties
        of implementation-defined attributes.

    8  an attribute_reference whose prefix statically denotes a
       statically constrained array object or array subtype, and whose
       attribute_designator is First, Last, or Length, with an optional
       dimension; {94-4968.a}

    9  a type_conversion whose subtype_mark denotes a static scalar
       subtype, and whose operand is a static expression;

   10  a qualified_expression whose subtype_mark denotes a static
       [(scalar or string)] subtype, and whose operand is a static
       expression; {94-4667.p}

 10.a   Ramification:  This rules out the subtype_mark'aggregate case.

 10.b   Reason:  Adding qualification to an expression shouldn't make it
        nonstatic, even for strings.

   11  a membership test whose simple_expression is a static expression,
       and whose range is a static range or whose subtype_mark denotes a
       static [(scalar or string)] subtype;

 11.a   Reason:  Clearly, we should allow membership tests in exactly
        the same cases where we allow qualified_expressions.

   12  a short-circuit control form both of whose relations are static
       expressions;

   13  a static expression enclosed in parentheses.

        13.a   Discussion:  {static (value)} Informally, we talk about a
        static value.  When we do, we mean a value specified by a static
        expression.

        13.b   Ramification:  The language requires a static expression in a
        number_declaration, a numeric type definition, a discrete_choice
        (sometimes), certain representation items, an attribute_designator,
        and when specifying the value of a discriminant governing a variant_
        part in a record_aggregate or extension_aggregate.

14   {statically (denote)} A name statically denotes an entity if it denotes
the entity and:

   15  It is a direct_name, expanded name, or character_literal, and it
       denotes a declaration other than a renaming_declaration; or

   16  It is an attribute_reference whose prefix statically denotes some
       entity; or

   17  It denotes a renaming_declaration with a name that statically
       denotes the renamed entity.

        17.a   Ramification:  Selected_components that are not expanded names
        and indexed_components do not statically denote things.

18   {static (function)} A static function is one of the following:

        18.a   Ramification:  These are the functions whose calls can be
        static expressions.

   19  a predefined operator whose parameter and result types are all
       scalar types none of which are descendants of formal scalar
       types;

   20  a predefined concatenation operator whose result type is a string
       type; {94-4679.a} {94-4684.a} {94-4687.a} {94-4738.a}

   21  an enumeration literal;

   22  a language-defined attribute that is a function, if the prefix
       denotes a static scalar subtype, and if the parameter and result
       types are scalar.

23   In any case, a generic formal subprogram is not a static function.

24   {static (constant)} A static constant is a constant view declared by a
full constant declaration or an object_renaming_declaration with a static
nominal subtype, having a value defined by a static scalar expression or by a
static string expression whose value has a length not exceeding the maximum
length of a string_literal in the implementation.

        24.a   Ramification:  A deferred constant is not static; the view
        introduced by the corresponding full constant declaration can be
        static.

        24.b   Reason:  The reason for restricting the length of static
        string constants is so that compilers don't have to store giant
        strings in their symbol tables.  Since most string constants will be
        initialized from string_literals, the length limit seems pretty
        natural.  The reason for avoiding nonstring types is also to save
        symbol table space.  We're trying to keep it cheap and simple (from
        the implementer's viewpoint), while still allowing, for example, the
        link name of a pragma Import to contain a concatenation.

        24.c   The length we're talking about is the maximum number of
        characters in the value represented by a string_literal, not the
        number of characters in the source representation; the quotes don't
        count.  {94-4747.b} {94-4748.b} {94-4754.b}

25   {static (range)} A static range is a range whose bounds are static
expressions, [or a range_attribute_reference that is equivalent to such a
range.]  {static (discrete_range)} A static discrete_range is one that is a
static range or is a subtype_indication that defines a static scalar subtype.
The base range of a scalar type is a static range, unless the type is a
descendant of a formal scalar type.

26   {static (subtype)} A static subtype is either a static scalar subtype or
a static string subtype.  {static (scalar subtype)} A static scalar subtype
is an unconstrained scalar subtype whose type is not a descendant of a formal
scalar type, or a constrained scalar subtype formed by imposing a compatible
static constraint on a static scalar subtype.  {static (string subtype)} A
static string subtype is an unconstrained string subtype whose index subtype
and component subtype are static (and whose type is not a descendant of a
formal array type), or a constrained string subtype formed by imposing a
compatible static constraint on a static string subtype.  {94-4539.a} In any
case, the subtype of a generic formal object of mode in out, and the result
subtype of a generic formal function, are not static.
        26.a   Ramification:  String subtypes are the only composite subtypes
        that can be static.

        26.b   Reason:  The part about generic formal objects of mode in out
        is necessary because the subtype of the formal is not required to
        have anything to do with the subtype of the actual.  For example:

26.c        subtype Int10 is Integer range 1..10;

26.d        generic
                F : in out Int10;
            procedure G;

26.e        procedure G is
            begin
                case F is
                    when 1..10 => null;
                    -- Illegal!
                end case;
            end G;

26.f        X : Integer range 1..20;
            procedure I is new G(F => X); -- OK.

        26.g   The case_statement is illegal, because the subtype of F is not
        static, so the choices have to cover all values of Integer, not just
        those in the range 1..10.  A similar issue arises for generic formal
        functions, now that function calls are object names.

27   {static (constraint)} The different kinds of static constraint are
defined as follows:

   28  A null constraint is always static;

   29  {static (range constraint)} {static (digits constraint)} {static
       (delta constraint)} A scalar constraint is static if it has no
       range_constraint, or one with a static range;

   30  {static (index constraint)} An index constraint is static if each
       discrete_range is static, and each index subtype of the
       corresponding array type is static;

   31  {static (discriminant constraint)} A discriminant constraint is
       static if each expression of the constraint is static, and the
       subtype of each discriminant is static.

32   {statically (constrained)} A subtype is statically constrained if it is
constrained, and its constraint is static.  An object is statically
constrained if its nominal subtype is statically constrained, or if it is a
static string constant.  {94-4776.c}


                               Legality Rules

33   A static expression is evaluated at compile time except when it is part
of the right operand of a static short-circuit control form whose value is
determined by its left operand.  This evaluation is performed exactly,
without performing Overflow_Checks.  For a static expression that is
evaluated:

   34  The expression is illegal if its evaluation fails a
       language-defined check other than Overflow_Check.

   35  If the expression is not part of a larger static expression, then
       its value shall be within the base range of its expected type.
       Otherwise, the value may be arbitrarily large or small.

   36  If the expression is of type universal_real and its expected type
       is a decimal fixed point type, then its value shall be a multiple
       of the small of the decimal type.

 36.a   Ramification:  This means that a numeric_literal for a decimal
        type cannot have ``extra'' significant digits.

37   The last two restrictions above do not apply if the expected type is a
descendant of a formal scalar type (or a corresponding actual type in an
instance).  {94-4926.a} {94-4929.a} {94-4950.a}

        37.a   Discussion:  Values outside the base range are not permitted
        when crossing from the ``static'' domain to the ``dynamic'' domain.
        This rule is designed to enhance portability of programs containing
        static expressions.  Note that this rule applies to the exact value,
        not the value after any rounding or truncation.  (See below for the
        rounding and truncation requirements.)

        37.b   Short-circuit control forms are a special case:

37.c        N: constant := 0.0;
            X: constant Boolean := (N = 0.0) or else (1.0/N > 0.5); -- Static.

        37.d   The declaration of X is legal, since the divide-by-zero part
        of the expression is not evaluated.  X is a static constant equal to
        True.

        37.e   Reason:  There is no requirement to recheck these rules in an
        instance; the base range check will generally be performed at run
        time anyway.


                         Implementation Requirements

38   For a real static expression that is not part of a larger static
expression, and whose expected type is not a descendant of a formal scalar
type, the implementation shall round or truncate the value (according to the
Machine_Rounds attribute of the expected type) to the nearest machine number
of the expected type; if the value is exactly half-way between two machine
numbers, any rounding shall be performed away from zero.  If the expected
type is a descendant of a formal scalar type, no special rounding or
truncating is required -- normal accuracy rules apply (see Annex G).

        38.a   Reason:  Discarding extended precision enhances portability by
        ensuring that the value of a static constant of a real type is always
        a machine number of the type.  Deterministic rounding of exact halves
        also enhances portability.

        38.b   When the expected type is a descendant of a formal floating
        point type, extended precision (beyond that of the machine numbers)
        can be retained when evaluating a static expression, to ease code
        sharing for generic instantiations.  For similar reasons, normal
        (nondeterministic) rounding or truncating rules apply for descendants
        of a formal fixed point type.

        38.c   Implementation Note:  Note that the implementation of static
        expressions has to keep track of plus and minus zero for a type whose
        Signed_Zeros attribute is True.  {94-4539.c}

        38.d   Note that the only values of a fixed point type are the
        multiples of the small, so a static conversion to a fixed-point type,
        or division by an integer, must do truncation to a multiple of small.
        It is not correct for the implementation to do all static
        calculations in infinite precision.


     NOTES
39   (28) An expression can be static even if it occurs in a context where
     staticness is not required.

   39.a   Ramification:  For example:

39.b        X : Float := Float'(1.0E+400) + 1.0 - Float'(1.0E+400);

   39.c   The expression is static, which means that the value of X must be
        exactly 1.0, independent of the accuracy or range of the run-time
        floating point implementation.

   39.d   The following kinds of expressions are never static:  explicit_
        dereference, indexed_component, slice, null, aggregate, allocator.

40   (29) A static (or run-time) type_conversion from a real type to an
     integer type performs rounding.  If the operand value is exactly
     half-way between two integers, the rounding is performed away from zero.

   40.a   Reason:  We specify this for portability.  The reason for not
        choosing round-to-nearest-even, for example, is that this method is
        easier to undo.

   40.b   Ramification:  The attribute Truncation (see A.5.3) can be used to
        perform a (static) truncation prior to conversion, to prevent
        rounding.

   40.c   Implementation Note:  The value of the literal
        0E999999999999999999999999999999999999999999999 is zero.  The
        implementation must take care to evaluate such literals properly.
        {94-5001.d} {94-5005.c}


                                  Examples

41   Examples of static expressions:

42  1 + 1       -- 2
    abs(-10)*3  -- 30

43  Kilo : constant := 1000;
    Mega : constant := Kilo*Kilo;   -- 1_000_000
    Long : constant := Float'Digits*2;

44  Half_Pi    : constant := Pi/2;           -- see 3.3.2
    Deg_To_Rad : constant := Half_Pi/90;
    Rad_To_Deg : constant := 1.0/Deg_To_Rad; -- equivalent to 1.0/((3.14159_265\
36/2)/90)


                            Extensions to Ada 83

        44.a   {extensions to Ada 83} The rules for static expressions and
        static subtypes are generalized to allow more kinds of
        compile-time-known expressions to be used where compile-time-known
        values are required, as follows:

         44.b  Membership tests and short-circuit control forms may
               appear in a static expression.

         44.c  The bounds and length of statically constrained array
               objects or subtypes are static.

         44.d  The Range attribute of a statically constrained array
               subtype or object gives a static range.

         44.e  A type_conversion is static if the subtype_mark denotes a
               static scalar subtype and the operand is a static
               expression.

         44.f  All numeric literals are now static, even if the expected
               type is a formal scalar type.  This is useful in case_
               statements and variant_parts, which both now allow a
               value of a formal scalar type to control the selection,
               to ease conversion of a package into a generic package.
               Similarly, named array aggregates are also permitted for
               array types with an index type that is a formal scalar
               type.

        44.g   The rules for the evaluation of static expressions are revised
        to require exact evaluation at compile time, and force a machine
        number result when crossing from the static realm to the dynamic
        realm, to enhance portability and predictability.  Exact evaluation
        is not required for descendants of a formal scalar type, to simplify
        generic code sharing and to avoid generic contract model problems.

        44.h   Static expressions are legal even if an intermediate in the
        expression goes outside the base range of the type.  Therefore, the
        following will succeed in Ada 9X, whereas it might raise an exception
        in Ada 83:

44.i        type Short_Int is range -32_768 .. 32_767;
            I : Short_Int := -32_768;

        44.j   This might raise an exception in Ada 83 because "32_768" is
        out of range, even though "-32_768" is not.  In Ada 9X, this will
        always succeed.

        44.k   Certain expressions involving string operations (in particular
        concatenation and membership tests) are considered static in Ada 9X.

        44.l   The reason for this change is to simplify the rule requiring
        compile-time-known string expressions as the link name in an
        interfacing pragma, and to simplify the preelaborability rules.

                        Incompatibilities With Ada 83

        44.m   {incompatibilities with Ada 83} An Ada 83 program that uses an
        out-of-range static value is illegal in Ada 9X, unless the expression
        is part of a larger static expression, or the expression is not
        evaluated due to being on the right-hand side of a short-circuit
        control form.

                         Wording Changes From Ada 83

        44.n   This clause (and 4.5.5, ``Multiplying Operators'') subsumes
        the RM83 section on Universal Expressions.

        44.o   The existence of static string expressions necessitated
        changing the definition of static subtype to include string subtypes.
        Most occurrences of "static subtype" have been changed to "static
        scalar subtype", in order to preserve the effect of the Ada 83 rules.
        This has the added benefit of clarifying the difference between
        "static subtype" and "statically constrained subtype", which has been
        a source of confusion.  In cases where we allow static string
        subtypes, we explicitly use phrases like "static string subtype" or
        "static (scalar or string) subtype", in order to clarify the meaning
        for those who have gotten used to the Ada 83 terminology.

        44.p   In Ada 83, an expression was considered nonstatic if it raised
        an exception.  Thus, for example:

44.q        Bad: constant := 1/0; -- Illegal!

        44.r   was illegal because 1/0 was not static.  In Ada 9X, the above
        example is still illegal, but for a different reason:  1/0 is static,
        but there's a separate rule forbidding the exception raising.



4.9.1 Statically Matching Constraints and Subtypes

                              Static Semantics

1   {statically matching (for constraints)} A constraint statically matches
another constraint if both are null constraints, both are static and have
equal corresponding bounds or discriminant values, or both are nonstatic and
result from the same elaboration of a constraint of a subtype_indication or
the same evaluation of a range of a discrete_subtype_definition.

2   {statically matching (for subtypes)} A subtype statically matches another
subtype of the same type if they have statically matching constraints.  Two
anonymous access subtypes statically match if their designated subtypes
statically match.

        2.a   Ramification:  Statically matching constraints and subtypes are
        the basis for subtype conformance of profiles (see 6.3.1).

3   {statically matching (for ranges)} Two ranges of the same type statically
match if both result from the same evaluation of a range, or if both are
static and have equal corresponding bounds.

        3.a   Ramification:  The notion of static matching of ranges is used
        in 12.5.3, ``Formal Array Types''; the index ranges of formal and
        actual constrained array subtypes have to statically match.

4   {statically compatible (for a constraint and a scalar subtype)} A
constraint is statically compatible with a scalar subtype if it statically
matches the constraint of the subtype, or if both are static and the
constraint is compatible with the subtype.  {statically compatible (for a
constraint and an access or composite subtype)} A constraint is statically
compatible with an access or composite subtype if it statically matches the
constraint of the subtype, or if the subtype is unconstrained.  {statically
compatible (for two subtypes)} One subtype is statically compatible with a
second subtype if the constraint of the first is statically compatible with
the second subtype.

        4.a   Discussion:  Static compatibility is required when constraining
        a parent subtype with a discriminant from a new discriminant_part.
        See 3.7.  Static compatibility is also used in matching generic
        formal derived types.

        4.b   Note that statically compatible with a subtype does not imply
        compatible with a type.  It is OK since the terms are used in
        different contexts.


                         Wording Changes From Ada 83

        4.c   This subclause is new to Ada 9X.



                            Section 5: Statements


1   [A statement defines an action to be performed upon its execution.]

2   [This section describes the general rules applicable to all statements.
Some statements are discussed in later sections:  Procedure_call_statements
and return_statements are described in Section 6, ``Subprograms''.  Entry_
call_statements, requeue_statements, delay_statements, accept_statements,
select_statements, and abort_statements are described in Section 9, ``Tasks
and Synchronization''.  Raise_statements are described in Section 11,
``Exceptions'', and code_statements in Section 13.  The remaining forms of
statements are presented in this section.]


                         Wording Changes From Ada 83

        2.a   The description of return_statements has been moved to 6.5,
        ``Return Statements'', so that it is closer to the description of
        subprograms.



5.1 Simple and Compound Statements - Sequences of Statements

1   [A statement is either simple or compound.  A simple_statement encloses
no other statement.  A compound_statement can enclose simple_statements and
other compound_statements.]


                                   Syntax

2   sequence_of_statements ::= statement {statement}

3   statement ::=
       {label} simple_statement | {label} compound_statement

4   simple_statement ::= null_statement
       | assignment_statement              | exit_statement
       | goto_statement                    | procedure_call_statement
       | return_statement                  | entry_call_statement
       | requeue_statement                 | delay_statement
       | abort_statement                   | raise_statement
       | code_statement

5   compound_statement ::=
         if_statement                      | case_statement
       | loop_statement                    | block_statement
       | accept_statement                  | select_statement

6   null_statement ::= null;

7   label ::= <<label_statement_identifier>>

8   statement_identifier ::= direct_name

    9   The direct_name of a statement_identifier shall be an identifier (not
    an operator_symbol).


                            Name Resolution Rules

10   The direct_name of a statement_identifier shall resolve to denote its
corresponding implicit declaration (see below).


                               Legality Rules

11   Distinct identifiers shall be used for all statement_identifiers that
appear in the same body, including inner block_statements but excluding inner
program units.
                              Static Semantics

12   For each statement_identifier, there is an implicit declaration (with
the specified identifier) at the end of the declarative_part of the innermost
block_statement or body that encloses the statement_identifier.  The implicit
declarations occur in the same order as the statement_identifiers occur in
the source text.  If a usage name denotes such an implicit declaration, the
entity it denotes is the label, loop_statement, or block_statement with the
given statement_identifier.

        12.a   Reason:  We talk in terms of individual statement_identifiers
        here rather than in terms of the corresponding statements, since a
        given statement may have multiple statement_identifiers.

        12.b   A block_statement that has no explicit declarative_part has an
        implicit empty declarative_part, so this rule can safely refer to the
        declarative_part of a block_statement.

        12.c   The scope of a declaration starts at the place of the
        declaration itself (see 8.2).  In the case of a label, loop, or block
        name, it follows from this rule that the scope of the implicit
        declaration starts before the first explicit occurrence of the
        corresponding name, since this occurrence is either in a statement
        label, a loop_statement, a block_statement, or a goto_statement.  An
        implicit declaration in a block_statement may hide a declaration
        given in an outer program unit or block_statement (according to the
        usual rules of hiding explained in 8.3).

        12.d   The syntax rule for label uses statement_identifier which is a
        direct_name (not a defining_identifier), because labels are
        implicitly declared.  The same applies to loop and block names.  In
        other words, the label itself is not the defining occurrence; the
        implicit declaration is.

        12.e   We cannot consider the label to be a defining occurrence.  An
        example that can tell the difference is this:

12.f        declare
                -- Label Foo is implicitly declared here.
            begin
                for Foo in ... loop
                    ...
                    <<Foo>> -- Illegal.
                    ...
                end loop;
            end;

        12.g   The label in this example is hidden from itself by the loop
        parameter with the same name; the example is illegal.  We considered
        creating a new syntactic category name, separate from direct_name and
        selector_name, for use in the case of statement labels.  However,
        that would confuse the rules in Section 8, so we didn't do it.


                              Dynamic Semantics

13   {execution [null_statement]} The execution of a null_statement has no
effect.

14   {transfer of control} A transfer of control is the run-time action of an
exit_statement, return_statement, goto_statement, or requeue_statement,
selection of a terminate_alternative, raising of an exception, or an abort,
which causes the next action performed to be one other than what would
normally be expected from the other rules of the language.  [As explained in
7.6.1, a transfer of control can cause the execution of constructs to be
completed and then left, which may trigger finalization.]

15   {execution [sequence_of_statements]} The execution of a sequence_of_
statements consists of the execution of the individual statements in
succession until the sequence_ is completed.

        15.a   Ramification:  It could be completed by reaching the end of
        it, or by a transfer of control.


     NOTES
16   (1) A statement_identifier that appears immediately within the
     declarative region of a named loop_statement or an accept_statement is
     nevertheless implicitly declared immediately within the declarative
     region of the innermost enclosing body or block_statement; in other
     words, the expanded name for a named statement is not affected by
     whether the statement occurs inside or outside a named loop or an
     accept_statement -- only nesting within block_statements is relevant to
     the form of its expanded name.

   16.a   Discussion:  Each comment in the following example gives the
        expanded name associated with an entity declared in the task body:

16.b        task body Compute is
               Sum : Integer := 0;                       -- Compute.Sum
            begin
             Outer:                                      -- Compute.Outer
               for I in 1..10 loop     -- Compute.Outer.I
                Blk:                                     -- Compute.Blk
                  declare
                     Sum : Integer := 0;                 -- Compute.Blk.Sum
                  begin
                     accept Ent(I : out Integer; J : in Integer) do
                                                         -- Compute.Ent.I, Comp\
ute.Ent.J
                        Compute.Ent.I := Compute.Outer.I;
                      Inner:                             -- Compute.Blk.Inner
                        for J in 1..10 loop
                                                         -- Compute.Blk.Inner.J
                           Sum := Sum + Compute.Blk.Inner.J * Compute.Ent.J;
                        end loop Inner;
                     end Ent;
                     Compute.Sum := Compute.Sum + Compute.Blk.Sum;
                  end Blk;
               end loop Outer;
               Record_Result(Sum);
            end Compute;


                                  Examples

17   Examples of labeled statements:

18  <<Here>> <<Ici>> <<Aqui>> <<Hier>> null;

19  <<After>> X := 1;


                            Extensions to Ada 83

        19.a   {extensions to Ada 83} The requeue_statement is new.

                         Wording Changes From Ada 83

        19.b   We define the syntactic category statement_identifier to
        simplify the description.  It is used for labels, loop names, and
        block names.  We define the entity associated with the implicit
        declarations of statement names.

        19.c   Completion includes completion caused by a transfer of
        control, although RM83-5.1(6) did not take this view.



5.2 Assignment Statements

1   [An assignment_statement replaces the current value of a variable with
the result of evaluating an expression.]


                                   Syntax

2   assignment_statement ::=
       variable_name := expression;


3   The execution of an assignment_statement includes the evaluation of the
expression and the assignment of the value of the expression into the target.
{assignment operation [distributed]} {assign: see assignment operation} [An
assignment operation (as opposed to an assignment_statement) is performed in
other contexts as well, including object initialization and by-copy parameter
passing.]  {target (of an assignment operation)} {target (of an assignment_
statement)} The target of an assignment operation is the view of the object
to which a value is being assigned; the target of an assignment_statement is
the variable denoted by the variable_name.

        3.a   Discussion:  Don't confuse this notion of the ``target'' of an
        assignment with the notion of the ``target object'' of an entry call
        or requeue.

        3.b   Don't confuse the term ``assignment operation'' with the
        assignment_statement.  The assignment operation is just one part of
        the execution of an assignment_statement.  The assignment operation
        is also a part of the execution of various other constructs; see
        7.6.1, ``Completion and Finalization'' for a complete list.  Note
        that when we say, ``such-and-such is assigned to so-and-so'', we mean
        that the assignment operation is being applied, and that so-and-so is
        the target of the assignment operation.


                            Name Resolution Rules

4   {expected type [assignment_statement variable_name]} The variable_name of
an assignment_statement is expected to be of any nonlimited type.  {expected
type [assignment_statement expression]} The expected type for the expression
is the type of the target.

        4.a   Implementation Note:  An assignment_statement as a whole is a
        "complete context," so if the variable_name of an assignment_
        statement is overloaded, the expression can be used to help
        disambiguate it.  For example:

4.b           type P1 is access R1;
              type P2 is access R2;

4.c           function F return P1;
              function F return P2;

4.d           X : R1;
            begin
              F.all := X;  -- Right hand side helps resolve left hand side


                               Legality Rules
5   The target [denoted by the variable_name] shall be a variable.

6   If the target is of a tagged class-wide type T'Class, then the expression
shall either be dynamically tagged, or of type T and tag-indeterminate (see
3.9.2).

        6.a   Reason:  This is consistent with the general rule that a single
        dispatching operation shall not have both dynamically tagged and
        statically tagged operands.  Note that for an object initialization
        (as opposed to the assignment_statement), a statically tagged
        initialization expression is permitted, since there is no chance for
        confusion (or Tag_Check failure).  Also, in an object initialization,
        tag-indeterminate expressions of any type covered by T'Class would be
        allowed, but with an assignment_statement, that might not work if the
        tag of the target was for a type that didn't have one of the
        dispatching operations in the tag-indeterminate expression.


                              Dynamic Semantics

7   {execution [assignment_statement]} For the execution of an assignment_
statement, the variable_name and the expression are first evaluated in an
arbitrary order.

        7.a   Ramification:  Other rules of the language may require that the
        bounds of the variable be determined prior to evaluating the
        expression, but that does not necessarily require evaluation of the
        variable_name, as pointed out by the ACID.

8   When the type of the target is class-wide:

    9  {controlling tag value [for the expression in an assignment_
       statement]} If the expression is tag-indeterminate (see 3.9.2),
       then the controlling tag value for the expression is the tag of
       the target;

 9.a    Ramification:  See 3.9.2, ``Dispatching Operations of Tagged
        Types''.

   10  {Tag_Check [partial]} {check, language-defined (Tag_Check)}
       {Constraint_Error (raised by failure of run-time check)}
       Otherwise [(the expression is dynamically tagged)], a check is
       made that the tag of the value of the expression is the same as
       that of the target; if this check fails, Constraint_Error is
       raised.

11   The value of the expression is converted to the subtype of the target.
[The conversion might raise an exception (see 4.6).]  {implicit subtype
conversion [assignment_statement]}

        11.a   Ramification:  4.6, ``Type Conversions'' defines what actions
        and checks are associated with subtype conversion.  For non-array
        subtypes, it is just a constraint check presuming the types match.
        For array subtypes, it checks the lengths and slides if the target is
        constrained.  ``Sliding'' means the array doesn't have to have the
        same bounds, so long as it is the same length.

12   In cases involving controlled types, the target is finalized, and an
anonymous object might be used as an intermediate in the assignment, as
described in 7.6.1, ``Completion and Finalization''.  {assignment operation}
{assignment operation (during execution of an assignment_statement)} In any
case, the converted value of the expression is then assigned to the target,
which consists of the following two steps:

        12.a   To be honest:  7.6.1 actually says that finalization happens
        always, but unless controlled types are involved, this finalization
        during an assignment_statement does nothing.

   13  The value of the target becomes the converted value.

   14  If any part of the target is controlled, its value is adjusted as
       explained in clause 7.6.  {adjustment [as part of assignment]}

 14.a   Ramification:  If any parts of the object are controlled, abort
        is deferred during the assignment operation itself, but not
        during the rest of the execution of an assignment_statement.


     NOTES
15   (2) The tag of an object never changes; in particular, an assignment_
     statement does not change the tag of the target.

16   (3) The values of the discriminants of an object designated by an access
     value cannot be changed (not even by assigning a complete value to the
     object itself) since such objects are always constrained; however,
     subcomponents of such objects may be unconstrained.

   16.a   Ramification:  The implicit subtype conversion described above for
        assignment_statements is performed only for the value of the
        right-hand side expression as a whole; it is not performed for
        subcomponents of the value.

   16.b   The determination of the type of the variable of an assignment_
        statement may require consideration of the expression if the variable
        name can be interpreted as the name of a variable designated by the
        access value returned by a function call, and similarly, as a
        component or slice of such a variable (see 8.6, ``The Context of
        Overload Resolution'').


                                  Examples

17   Examples of assignment statements:

18  Value := Max_Value - 1;
    Shade := Blue;

19  Next_Frame(F)(M, N) := 2.5;        --  see 4.1.1
    U := Dot_Product(V, W);            --  see 6.3

20  Writer := (Status => Open, Unit => Printer, Line_Count => 60);  -- see 3.8.1
    Next_Car.all := (72074, null);    --  see 3.10.1

21   Examples involving scalar subtype conversions:

22  I, J : Integer range 1 .. 10 := 5;
    K    : Integer range 1 .. 20 := 15;
     ...

23  I := J;  --  identical ranges
    K := J;  --  compatible ranges
    J := K;  --  will raise Constraint_Error if K > 10

24   Examples involving array subtype conversions:

25  A : String(1 .. 31);
    B : String(3 .. 33);
     ...

26  A := B;  --  same number of components

27  A(1 .. 9)  := "tar sauce";
    A(4 .. 12) := A(1 .. 9);  --  A(1 .. 12) = "tartar sauce"


     NOTES
28   (4) Notes on the examples:  Assignment_statements are allowed even in
     the case of overlapping slices of the same array, because the
     variable_name and expression are both evaluated before copying the value
     into the variable.  In the above example, an implementation yielding A(1
     .. 12) = "tartartartar" would be incorrect.


                            Extensions to Ada 83

        28.a   {extensions to Ada 83} We now allow user-defined finalization
        and value adjustment actions as part of assignment_statements (see
        7.6, ``User-Defined Assignment and Finalization'').

                         Wording Changes From Ada 83

        28.b   The special case of array assignment is subsumed by the
        concept of a subtype conversion, which is applied for all kinds of
        types, not just arrays.  For arrays it provides ``sliding.''  For
        numeric types it provides conversion of a value of a universal type
        to the specific type of the target.  For other types, it generally
        has no run-time effect, other than a constraint check.

        28.c   We now cover in a general way in 3.7.2 the erroneous execution
        possible due to changing the value of a discriminant when the
        variable in an assignment_statement is a subcomponent that depends on
        discriminants.



5.3 If Statements

1   [An if_statement selects for execution at most one of the enclosed
sequences_of_statements, depending on the (truth) value of one or more
corresponding conditions.]


                                   Syntax

2   if_statement ::=
        if condition then
          sequence_of_statements
       {elsif condition then
          sequence_of_statements}
       [else
          sequence_of_statements]
        end if;

3   condition ::= boolean_expression


                            Name Resolution Rules

4   {expected type [condition]} A condition is expected to be of any boolean
type.


                              Dynamic Semantics

5   {execution [if_statement]} For the execution of an if_statement, the
condition specified after if, and any conditions specified after elsif, are
evaluated in succession (treating a final else as elsif True then), until one
evaluates to True or all conditions are evaluated and yield False.  If a
condition evaluates to True, then the corresponding sequence_of_statements is
executed; otherwise none of them is executed.
        5.a   Ramification:  The part about all evaluating to False can't
        happen if there is an else, since that is herein considered
        equivalent to elsif True then.


                                  Examples

6   Examples of if statements:

7   if Month = December and Day = 31 then
       Month := January;
       Day   := 1;
       Year  := Year + 1;
    end if;

8   if Line_Too_Short then
       raise Layout_Error;
    elsif Line_Full then
       New_Line;
       Put(Item);
    else
       Put(Item);
    end if;

9   if My_Car.Owner.Vehicle /= My_Car then            --  see 3.10.1
       Report ("Incorrect data");
    end if;



5.4 Case Statements

1   [A case_statement selects for execution one of a number of alternative
sequences_of_statements; the chosen alternative is defined by the value of an
expression.]


                                   Syntax

2   case_statement ::=
       case expression is
           case_statement_alternative
          {case_statement_alternative}
       end case;

3   case_statement_alternative ::=
       when discrete_choice_list =>
          sequence_of_statements


                            Name Resolution Rules

4   {expected type [case expression]} The expression is expected to be of any
discrete type.  {expected type [case_statement_alternative discrete_choice]}
The expected type for each discrete_choice is the type of the expression.


                               Legality Rules

5   The expressions and discrete_ranges given as discrete_choices of a case_
statement shall be static.  [A discrete_choice others, if present, shall
appear alone and in the last discrete_choice_list.]

6   The possible values of the expression shall be covered as follows:

    7  If the expression is a name [(including a type_conversion or a
       function_call)] having a static and constrained nominal subtype,
       or is a qualified_expression whose subtype_mark denotes a static
       and constrained scalar subtype, then each non-others discrete_
       choice shall cover only values in that subtype, and each value of
       that subtype shall be covered by some discrete_choice [(either
       explicitly or by others)].

 7.a    Ramification:  Although not official names of objects, a value
        conversion still has a defined nominal subtype, namely its
        target subtype.  See 4.6.

    8  If the type of the expression is root_integer, universal_integer,
       or a descendant of a formal scalar type, then the case_statement
       shall have an others discrete_choice.

 8.a    Reason:  This is because the base range is implementation
        defined for root_integer and universal_integer, and not known
        statically in the case of a formal scalar type.

    9  Otherwise, each value of the base range of the type of the
       expression shall be covered [(either explicitly or by others)].

10   Two distinct discrete_choices of a case_statement shall not cover the
same value.

        10.a   Ramification:  The goal of these coverage rules is that any
        possible value of the expression of a case_statement should be
        covered by exactly one discrete_choice of the case_statement, and
        that this should be checked at compile time.  The goal is achieved in
        most cases, but there are two minor loopholes:

         10.b  If the expression reads an object with an invalid
               representation (e.g. an uninitialized object), then the
               value can be outside the covered range.  This can happen
               for static constrained subtypes, as well as nonstatic or
               unconstrained subtypes.  It cannot, however, happen if
               the case_statement has the discrete_choice others,
               because others covers all values, even those outside the
               subtype.

         10.c  If the compiler chooses to represent the value of an
               expression of an unconstrained subtype in a way that
               includes values outside the bounds of the subtype, then
               those values can be outside the covered range.  For
               example, if X: Integer := Integer'Last;, and the case
               expression is X+1, then the implementation might choose
               to produce the correct value, which is outside the bounds
               of Integer.  (It might raise Constraint_Error instead.)
               This case can only happen for non-generic subtypes that
               are either unconstrained or non-static (or both).  It can
               only happen if there is no others discrete_choice.

        10.d   In the uninitialized variable case, the value might be
        anything; hence, any alternative can be chosen, or Constraint_Error
        can be raised.  (We intend to prevent, however, jumping to random
        memory locations and the like.)  In the out-of-range case, the
        behavior is more sensible: if there is an others, then the
        implementation may choose to raise Constraint_Error on the evaluation
        of the expression (as usual), or it may choose to correctly evaluate
        the expression and therefore choose the others alternative.
        Otherwise (no others), Constraint_Error is raised either way -- on
        the expression evaluation, or for the case_statement itself.

        10.e   For an enumeration type with a discontiguous set of internal
        codes (see 13.4), the only way to get values in between the proper
        values is via an object with an invalid representation; there is no
        ``out-of-range'' situation that can produce them.


                              Dynamic Semantics

11   {execution [case_statement]} For the execution of a case_statement the
expression is first evaluated.

12   If the value of the expression is covered by the discrete_choice_list of
some case_statement_alternative, then the sequence_of_statements of the
_alternative is executed.

13   {Overflow_Check [partial]} {check, language-defined (Overflow_Check)}
{Constraint_Error (raised by failure of run-time check)} Otherwise (the value
is not covered by any discrete_choice_list, perhaps due to being outside the
base range), Constraint_Error is raised.  {94-4768.e}

        13.a   Ramification:  In this case, the value is outside the base
        range of its type, or is an invalid representation.


     NOTES
14   (5) The execution of a case_statement chooses one and only one
     alternative.  Qualification of the expression of a case_statement by a
     static subtype can often be used to limit the number of choices that
     need be given explicitly.


                                  Examples

15   Examples of case statements:

16  case Sensor is
       when Elevation  => Record_Elevation(Sensor_Value);
       when Azimuth    => Record_Azimuth  (Sensor_Value);
       when Distance   => Record_Distance (Sensor_Value);
       when others     => null;
    end case;

17
    case Today is
       when Mon        => Compute_Initial_Balance;
       when Fri        => Compute_Closing_Balance;
       when Tue .. Thu => Generate_Report(Today);
       when Sat .. Sun => null;
    end case;

18
    case Bin_Number(Count) is
       when 1      => Update_Bin(1);
       when 2      => Update_Bin(2);
       when 3 | 4  =>
          Empty_Bin(1);
          Empty_Bin(2);
       when others => raise Error;
    end case;


                            Extensions to Ada 83

        18.a   {extensions to Ada 83} In Ada 83, the expression in a case_
        statement is not allowed to be of a generic formal type.  This
        restriction is removed in Ada 9X; an others discrete_choice is
        required instead.

        18.b   In Ada 9X, a function call is the name of an object; this was
        not true in Ada 83 (see 4.1, ``Names'').  This change makes the
        following case_statement legal:
18.c        subtype S is Integer range 1..2;
            function F return S;
            case F is
               when 1 => ...;
               when 2 => ...;
               -- No others needed.
            end case;

        18.d   Note that the result subtype given in a function renaming_
        declaration is ignored; for a case_statement whose expression calls a
        such a function, the full coverage rules are checked using the result
        subtype of the original function.  Note that predefined operators
        such as "+" have an unconstrained result subtype (see 4.5.1).  Note
        that generic formal functions do not have static result subtypes.
        Note that the result subtype of an inherited subprogram need not
        correspond to any namable subtype; there is still a perfectly good
        result subtype, though.

                         Wording Changes From Ada 83

        18.e   Ada 83 forgot to say what happens for ``legally''
        out-of-bounds values.

        18.f   We take advantage of rules and terms (e.g. cover a value)
        defined for discrete_choices and discrete_choice_lists in 3.8.1,
        ``Variant Parts and Discrete Choices''.

        18.g   In the Name Resolution Rule for the case expression, we no
        longer need RM83-5.4(3)'s ``which must be determinable independently
        of the context in which the expression occurs, but using the fact
        that the expression must be of a discrete type,'' because the
        expression is now a complete context.  See 8.6, ``The Context of
        Overload Resolution''.

        18.h   Since type_conversions are now defined as names, their
        coverage rule is now covered under the general rule for names, rather
        than being separated out along with qualified_expressions.



5.5 Loop Statements

1   [A loop_statement includes a sequence_of_statements that is to be
executed repeatedly, zero or more times.]


                                   Syntax

2   loop_statement ::=
       [loop_statement_identifier:]
          [iteration_scheme] loop
             sequence_of_statements
           end loop [loop_identifier];

3   iteration_scheme ::= while condition
       | for loop_parameter_specification

4   loop_parameter_specification ::=
       defining_identifier in [reverse] discrete_subtype_definition

    5   If a loop_statement has a loop_statement_identifier, then the
    identifier shall be repeated after the end loop; otherwise, there shall
    not be an identifier after the end loop.


                              Static Semantics

6   {loop parameter} A loop_parameter_specification declares a loop
parameter, which is an object whose subtype is that defined by the discrete_
subtype_definition.  {parameter: see also loop parameter}


                              Dynamic Semantics

7   {execution [loop_statement]} For the execution of a loop_statement, the
sequence_of_statements is executed repeatedly, zero or more times, until the
loop_statement is complete.  The loop_statement is complete when a transfer
of control occurs that transfers control out of the loop, or, in the case of
an iteration_scheme, as specified below.

8   {execution [loop_statement with a while iteration_scheme]} For the
execution of a loop_statement with a while iteration_scheme, the condition is
evaluated before each execution of the sequence_of_statements; if the value
of the condition is True, the sequence_of_statements is executed; if False,
the execution of the loop_statement is complete.

9   {execution [loop_statement with a for iteration_scheme]} {elaboration
[loop_parameter_specification]} For the execution of a loop_statement with a
for iteration_scheme, the loop_parameter_specification is first elaborated.
This elaboration creates the loop parameter and elaborates the discrete_
subtype_definition.  If the discrete_subtype_definition defines a subtype
with a null range, the execution of the loop_statement is complete.
Otherwise, the sequence_of_statements is executed once for each value of the
discrete subtype defined by the discrete_subtype_definition (or until the
loop is left as a consequence of a transfer of control).  {assignment
operation (during execution of a for loop)} Prior to each such iteration, the
corresponding value of the discrete subtype is assigned to the loop
parameter.  These values are assigned in increasing order unless the reserved
word reverse is present, in which case the values are assigned in decreasing
order.

        9.a   Ramification:  The order of creating the loop parameter and
        evaluating the discrete_subtype_definition doesn't matter, since the
        creation of the loop parameter has no side effects (other than
        possibly raising Storage_Error, but anything can do that).


     NOTES
10   (6) A loop parameter is a constant; it cannot be updated within the
     sequence_of_statements of the loop (see 3.3).

11   (7) An object_declaration should not be given for a loop parameter,
     since the loop parameter is automatically declared by the loop_
     parameter_specification.  The scope of a loop parameter extends from the
     loop_parameter_specification to the end of the loop_statement, and the
     visibility rules are such that a loop parameter is only visible within
     the sequence_of_statements of the loop.

   11.a   Implementation Note:  An implementation could give a warning if a
        variable is hidden by a loop_parameter_specification.

12   (8) The discrete_subtype_definition of a for loop is elaborated just
     once.  Use of the reserved word reverse does not alter the discrete
     subtype defined, so that the following iteration_schemes are not
     equivalent; the first has a null range.

13       for J in reverse 1 ..  0
         for J in 0 .. 1

   13.a   Ramification:  If a loop_parameter_specification has a static
        discrete range, the subtype of the loop parameter is static.


                                  Examples

14   Example of a loop statement without an iteration scheme:

15  loop
       Get(Current_Character);
       exit when Current_Character = '*';
    end loop;

16   Example of a loop statement with a while iteration scheme:

17  while Bid(N).Price < Cut_Off.Price loop
       Record_Bid(Bid(N).Price);
       N := N + 1;
    end loop;

18   Example of a loop statement with a for iteration scheme:

19  for J in Buffer'Range loop     --  works even with a null range
       if Buffer(J) /= Space then
          Put(Buffer(J));
       end if;
    end loop;

20   Example of a loop statement with a name:

21  Summation:
       while Next /= Head loop       -- see 3.10.1
          Sum  := Sum + Next.Value;
          Next := Next.Succ;
       end loop Summation;


                         Wording Changes From Ada 83

        21.a   The constant-ness of loop parameters is specified in 3.3,
        ``Objects and Named Numbers''.



5.6 Block Statements

1   [A block_statement encloses a handled_sequence_of_statements optionally
preceded by a declarative_part.]


                                   Syntax

2   block_statement ::=
       [block_statement_identifier:]
           [declare
                declarative_part]
            begin
                handled_sequence_of_statements
            end [block_identifier];

    3   If a block_statement has a block_statement_identifier, then the
    identifier shall be repeated after the end; otherwise, there shall not be
    an identifier after the end.


                              Static Semantics

4   A block_statement that has no explicit declarative_part has an implicit
empty declarative_part.
        4.a   Ramification:  Thus, other rules can always refer to the
        declarative_part of a block_statement.


                              Dynamic Semantics

5   {execution [block_statement]} The execution of a block_statement consists
of the elaboration of its declarative_part followed by the execution of its
handled_sequence_of_statements.


                                  Examples

6   Example of a block statement with a local variable:

7   Swap:
       declare
          Temp : Integer;
       begin
          Temp := V; V := U; U := Temp;
       end Swap;

        7.a   Ramification:  If task objects are declared within a block_
        statement whose execution is completed, the block_statement is not
        left until all its dependent tasks are terminated (see 7.6).  This
        rule applies to completion caused by a transfer of control.

        7.b   Within a block_statement, the block name can be used in
        expanded names denoting local entities such as Swap.Temp in the above
        example (see 4.1.3).


                         Wording Changes From Ada 83

        7.c   The syntax rule for block_statement now uses the syntactic
        category handled_sequence_of_statements.



5.7 Exit Statements

1   [An exit_statement is used to complete the execution of an enclosing
loop_statement; the completion is conditional if the exit_statement includes
a condition.]  {94-4605.a} {94-4560.a}


                                   Syntax

2   exit_statement ::=
       exit [loop_name] [when condition];


                            Name Resolution Rules

3   The loop_name, if any, in an exit_statement shall resolve to denote a
loop_statement.


                               Legality Rules

4   {apply (to a loop_statement by an exit_statement)} Each exit_statement
applies to a loop_statement; this is the loop_statement being exited.  An
exit_statement with a name is only allowed within the loop_statement denoted
by the name, and applies to that loop_statement.  An exit_statement without a
name is only allowed within a loop_statement, and applies to the innermost
enclosing one.  An exit_statement that applies to a given loop_statement
shall not appear within a body or accept_statement, if this construct is
itself enclosed by the given loop_statement.


                              Dynamic Semantics

5   {execution [exit_statement]} For the execution of an exit_statement, the
condition, if present, is first evaluated.  If the value of the condition is
True, or if there is no condition, a transfer of control is done to complete
the loop_statement.  If the value of the condition is False, no transfer of
control takes place.


     NOTES
6    (9) Several nested loops can be exited by an exit_statement that names
     the outer loop.


                                  Examples

7   Examples of loops with exit statements:

8   for N in 1 .. Max_Num_Items loop
       Get_New_Item(New_Item);
       Merge_Item(New_Item, Storage_File);
       exit when New_Item = Terminal_Item;
    end loop;

9   Main_Cycle:
       loop
          --  initial statements
          exit Main_Cycle when Found;
          --  final statements
       end loop Main_Cycle;



5.8 Goto Statements

1   [A goto_statement specifies an explicit transfer of control from this
statement to a target statement with a given label.]


                                   Syntax

2   goto_statement ::= goto label_name;


                            Name Resolution Rules

3   {target statement (of a goto_statement)} The label_name shall resolve to
denote a label; the statement with that label is the target statement.


                               Legality Rules

4   The innermost sequence_of_statements that encloses the target statement
shall also enclose the goto_statement.

        4.a   Ramification:  The goto_statement can be a statement of an
        inner sequence_.

Furthermore, if a goto_statement is enclosed by an accept_statement or a
body, then the target statement shall not be outside this enclosing
construct.

        4.b   Ramification:  It follows from the previous rule that if the
        target statement is enclosed by such a construct, then the goto_
        statement cannot be outside.


                              Dynamic Semantics

5   {execution [goto_statement]} The execution of a goto_statement transfers
control to the target statement, completing the execution of any compound_
statement that encloses the goto_statement but does not enclose the target.


     NOTES
6    (10) The above rules allow transfer of control to a statement of an
     enclosing sequence_of_statements but not the reverse.  Similarly, they
     prohibit transfers of control such as between alternatives of a case_
     statement, if_statement, or select_statement; between exception_
     handlers; or from an exception_handler of a handled_sequence_of_
     statements back to its sequence_of_statements.


                                  Examples

7   Example of a loop containing a goto statement:

8   <<Sort>>
    for I in 1 .. N-1 loop
       if A(I) > A(I+1) then
          Exchange(A(I), A(I+1));
          goto Sort;
       end if;
    end loop;



                           Section 6: Subprograms


1   {subprogram} {procedure} {function} A subprogram is a program unit or
intrinsic operation whose execution is invoked by a subprogram call.  There
are two forms of subprogram: procedures and functions.  A procedure call is a
statement; a function call is an expression and returns a value.  The
definition of a subprogram can be given in two parts:  a subprogram
declaration defining its interface, and a subprogram_body defining its
execution.  [Operators and enumeration literals are functions.]

        1.a   To be honest:  A function call is an expression, but more
        specifically it is a name.

2   {callable entity} A callable entity is a subprogram or entry (see Section
9).  {call} A callable entity is invoked by a call; that is, a subprogram
call or entry call.  {callable construct} A callable construct is a construct
that defines the action of a call upon a callable entity:  a subprogram_body,
entry_body, or accept_statement.

        2.a   Ramification:  Note that ``callable entity'' includes
        predefined operators, enumeration literals, and abstract subprograms.
        ``Call'' includes calls of these things.  They do not have callable
        constructs, since they don't have completions.



6.1 Subprogram Declarations

1   [A subprogram_declaration declares a procedure or function.]
                                   Syntax

2   subprogram_declaration ::= subprogram_specification;

3   abstract_subprogram_declaration ::= subprogram_specification is abstract;

4   subprogram_specification ::=
         procedure defining_program_unit_name  parameter_profile
       | function defining_designator  parameter_and_result_profile

5   designator ::= [parent_unit_name . ]identifier | operator_symbol

6   defining_designator ::= defining_program_unit_name | defining_operator_symb\
ol

7   defining_program_unit_name ::= [parent_unit_name . ]defining_identifier

    8   [The optional parent_unit_name is only allowed for library units (see
    10.1.1).]


9   operator_symbol ::= string_literal

    10   The sequence of characters in an operator_symbol shall correspond to
    an operator belonging to one of the six classes of operators defined in
    clause 4.5 (spaces are not allowed and the case of letters is not
    significant).


11  defining_operator_symbol ::= operator_symbol

12  parameter_profile ::= [formal_part]

13  parameter_and_result_profile ::= [formal_part] return subtype_mark

14  formal_part ::=
       (parameter_specification {; parameter_specification})

15  parameter_specification ::=
        defining_identifier_list : mode  subtype_mark [:= default_expression]
      | defining_identifier_list : access_definition [:= default_expression]

16  mode ::= [in] | in out | out


                            Name Resolution Rules

17   {formal parameter (of a subprogram)} A formal parameter is an object
[directly visible within a subprogram_body] that represents the actual
parameter passed to the subprogram in a call; it is declared by a parameter_
specification.  {expected type [parameter default_expression]} For a formal
parameter, the expected type for its default_expression, if any, is that of
the formal parameter.  {parameter: see formal parameter}


                               Legality Rules

18   {parameter mode} The parameter mode of a formal parameter conveys the
direction of information transfer with the actual parameter:  in, in out, or
out.  Mode in is the default, and is the mode of a parameter defined by an
access_definition.  The formal parameters of a function, if any, shall have
the mode in.

        18.a   Ramification:  Access parameters are permitted.  This
        restriction to in parameters is primarily a methodological
        restriction, though it also simplifies implementation for some
        compiler technologies.

19   A default_expression is only allowed in a parameter_specification for a
formal parameter of mode in.

20   {requires a completion [subprogram_declaration]} {requires a completion
[generic_subprogram_declaration]} A subprogram_declaration or a generic_
subprogram_declaration requires a completion:  [a body, a renaming_
declaration (see 8.5), or a pragma Import (see B.1)].  [A completion is not
allowed for an abstract_subprogram_declaration.]

        20.a   Ramification:  Abstract subprograms are not declared by
        subprogram_declarations, and so do not require completion.  Protected
        subprograms are declared by subprogram_declarations, and so require
        completion.  Note that an abstract subprogram is a subprogram, and a
        protected subprogram is a subprogram, but a generic subprogram is not
        a subprogram.

21   A name that denotes a formal parameter is not allowed within the formal_
part in which it is declared, nor within the formal_part of a corresponding
body or accept_statement.

        21.a   Ramification:  By contrast, generic_formal_parameter_declara-
        tions are visible to subsequent declarations in the same generic_
        formal_part.


                              Static Semantics

22   {profile} The profile of (a view of) a callable entity is either a
parameter_profile or parameter_and_result_profile[; it embodies information
about the interface to that entity -- for example, the profile includes
information about parameters passed to the callable entity.  All callable
entities have a profile -- enumeration literals, other subprograms, and
entries.  An access-to-subprogram type has a designated profile.]  Associated
with a profile is a calling convention.  A subprogram_declaration declares a
procedure or a function, as indicated by the initial reserved word, with name
and profile as given by its specification.

23   {nominal subtype [of a formal parameter]} The nominal subtype of a
formal parameter is the subtype denoted by the subtype_mark, or defined by
the access_definition, in the parameter_specification.

24   {access parameter} An access parameter is a formal in parameter
specified by an access_definition.  An access parameter is of an anonymous
general access-to-variable type (see 3.10).  [Access parameters allow
dispatching calls to be controlled by access values.]

25   {subtypes (of a profile)} The subtypes of a profile are:

   26  For any non-access parameters, the nominal subtype of the
       parameter.

   27  For any access parameters, the designated subtype of the
       parameter type.

   28  For any result, the result subtype.

29   [{types (of a profile)} The types of a profile are the types of those
subtypes.]

30   [A subprogram declared by an abstract_subprogram_declaration is
abstract; a subprogram declared by a subprogram_declaration is not.  See
3.9.3, ``Abstract Types and Subprograms''.]


                              Dynamic Semantics

31   {elaboration [subprogram_declaration]} {elaboration [abstract_
subprogram_declaration]} The elaboration of a subprogram_declaration or an
abstract_subprogram_declaration has no effect.


     NOTES
32   (1) A parameter_specification with several identifiers is equivalent to
     a sequence of single parameter_specifications, as explained in 3.3.

33   (2) Abstract subprograms do not have bodies, and cannot be used in a
     nondispatching call (see 3.9.3, ``Abstract Types and Subprograms'').

34   (3) The evaluation of default_expressions is caused by certain calls, as
     described in 6.4.1.  They are not evaluated during the elaboration of
     the subprogram declaration.

35   (4) Subprograms can be called recursively and can be called concurrently
     from multiple tasks.


                                  Examples

36   Examples of subprogram declarations:

37  procedure Traverse_Tree;
    procedure Increment(X : in out Integer);
    procedure Right_Indent(Margin : out Line_Size);          --  see 3.5.4
    procedure Switch(From, To : in out Link);                --  see 3.10.1

38  function Random return Probability;                      --  see 3.5.7

39  function Min_Cell(X : Link) return Cell;                 --  see 3.10.1
    function Next_Frame(K : Positive) return Frame;          --  see 3.10
    function Dot_Product(Left, Right : Vector) return Real;  --  see 3.6

40  function "*"(Left, Right : Matrix) return Matrix;        --  see 3.6

41   Examples of in parameters with default expressions:

42  procedure Print_Header(Pages  : in Natural;
                Header : in Line    :=  (1 .. Line'Last => ' ');  --  see 3.6
                Center : in Boolean := True);


                            Extensions to Ada 83

        42.a   {extensions to Ada 83} The syntax for abstract_subprogram_
        declaration is added.  The syntax for parameter_specification is
        revised to allow for access parameters (see 3.10)

        42.b   Program units that are library units may have a parent_unit_
        name to indicate the parent of a child (see Section 10).

                         Wording Changes From Ada 83

        42.c   We have incorporated the rules from RM83-6.5, ``Function
        Subprograms'' here and in 6.3, ``Subprogram Bodies''

        42.d   We have incorporated the definitions of RM83-6.6, ``Parameter
        and Result Type Profile - Overloading of Subprograms'' here.

        42.e   The syntax rule for defining_operator_symbol is new.  It is
        used for the defining occurrence of an operator_symbol, analogously
        to defining_identifier.  Usage occurrences use the direct_name or
        selector_name syntactic categories.  The syntax rules for defining_
        designator and defining_program_unit_name are new.
6.2 Formal Parameter Modes

1   [A parameter_specification declares a formal parameter of mode in, in
out, or out.]


                              Static Semantics

2   {pass by copy} {by copy parameter passing} {copy parameter passing} {pass
by reference} {by reference parameter passing} {reference parameter passing}
A parameter is passed either by copy or by reference.  [When a parameter is
passed by copy, the formal parameter denotes a separate object from the
actual parameter, and any information transfer between the two occurs only
before and after executing the subprogram.  When a parameter is passed by
reference, the formal parameter denotes (a view of) the object denoted by the
actual parameter; reads and updates of the formal parameter directly
reference the actual parameter object.]

3   {by-copy type} A type is a by-copy type if it is an elementary type, or
if it is a descendant of a private type whose full type is a by-copy type.  A
parameter of a by-copy type is passed by copy.

4   {by-reference type} A type is a by-reference type if it is a descendant
of one of the following:

    5  a tagged type;

    6  a task or protected type;

    7  a nonprivate type with the reserved word limited in its
       declaration;

 7.a    Ramification:  A limited private type is by-reference only if it
        falls under one of the other categories.

    8  a composite type with a subcomponent of a by-reference type;

    9  a private type whose full type is a by-reference type.

10   A parameter of a by-reference type is passed by reference.  {associated
object (of a value of a by-reference type)} Each value of a by-reference type
has an associated object.  For a parenthesized expression, qualified_
expression, or type_conversion, this object is the one associated with the
operand.  {94-4774.a}

        10.a   Ramification:  By-reference parameter passing makes sense only
        if there is an object to reference; hence, we define such an object
        for each case.

        10.b   Since tagged types are by-reference types, this implies that
        every value of a tagged type has an associated object.  This
        simplifies things, because we can define the tag to be a property of
        the object, and not of the value of the object, which makes it
        clearer that object tags never change.

        10.c   We considered simplifying things even more by making every
        value (and therefore every expression) have an associated object.
        After all, there is little semantic difference between a constant
        object and a value.  However, this would cause problems for untagged
        types.  In particular, we would have to do a constraint check on
        every read of a type conversion (or a renaming thereof) in certain
        cases.

        10.d   We do not want this definition to depend on the view of the
        type; privateness is essentially ignored for this definition.
        Otherwise, things would be confusing (does the rule apply at the call
        site, at the site of the declaration of the subprogram, at the site
        of the return_statement?), and requiring different calls to use
        different mechanisms would be an implementation burden.

        10.e   C.6, ``Shared Variable Control'' says that a composite type
        with an atomic or volatile subcomponent is a by-reference type, among
        other things.

        10.f   {associated object (of a value of a limited type)} Every value
        of a limited by-reference type is the value of one and only one
        limited object.  The associated object of a value of a limited
        by-reference type is the object whose value it represents.  {same
        value (for a limited type)} Two values of a limited by-reference type
        are the same if and only if they represent the value of the same
        object.

        10.g   We say ``by-reference'' above because these statements are not
        always true for limited private types whose underlying type is
        nonlimited (unfortunately).

11   {unspecified [partial]} For parameters of other types, it is unspecified
whether the parameter is passed by copy or by reference.

        11.a   Discussion:  There is no need to incorporate the discussion of
        AI-00178, which requires pass-by-copy for certain kinds of actual
        parameters, while allowing pass-by-reference for others.  This is
        because we explicitly indicate that a function creates an anonymous
        constant object for its result, unless the type is a
        return-by-reference type (see 6.5).  We also provide a special
        dispensation for instances of Unchecked_Conversion to return by
        reference, even if the result type is not a return-by-reference type
        (see 13.9).


                          Bounded (Run-Time) Errors

12   {bounded error} {distinct access paths} {access paths (distinct)}
{aliasing: see distinct access paths} If one name denotes a part of a formal
parameter, and a second name denotes a part of a distinct formal parameter or
an object that is not part of a formal parameter, then the two names are
considered distinct access paths.  If an object is of a type for which the
parameter passing mechanism is not specified, then it is a bounded error to
assign to the object via one access path, and then read the value of the
object via a distinct access path, unless the first access path denotes a
part of a formal parameter that no longer exists at the point of the second
access [(due to leaving the corresponding callable construct).]  {94-4573.a}
{94-4572.a} {94-4751.a} {94-4572.b} {94-4751.b} {94-4572.c} {94-4751.c}
{Program_Error (raised by failure of run-time check)} The possible
consequences are that Program_Error is raised, or the newly assigned value is
read, or some old value of the object is read.

        12.a   Discussion:  For example, if we call ``P(X => Global_Variable,
        Y => Global_Variable)'', then within P, the names ``X'', ``Y'', and
        ``Global_Variable'' are all distinct access paths.  If Global_
        Variable's type is neither pass-by-copy nor pass-by-reference, then
        it is a bounded error to assign to Global_Variable and then read X or
        Y, since the language does not specify whether the old or the new
        value would be read.  On the other hand, if Global_Variable's type is
        pass-by-copy, then the old value would always be read, and there is
        no error.  Similarly, if Global_Variable's type is defined by the
        language to be pass-by-reference, then the new value would always be
        read, and again there is no error.

        12.b   Reason:  We are saying assign here, not update, because
        updating any subcomponent is considered to update the enclosing
        object.

        12.c   The ``still exists'' part is so that a read after the
        subprogram returns is OK.

        12.d   If the parameter is of a by-copy type, then there is no issue
        here -- the formal is not a view of the actual.  If the parameter is
        of a by-reference type, then the programmer may depend on updates
        through one access path being visible through some other access path,
        just as if the parameter were of an access type.

        12.e   Implementation Note:  The implementation can keep a copy in a
        register of a parameter whose parameter-passing mechanism is not
        specified.  If a different access path is used to update the object
        (creating a bounded error situation), then the implementation can
        still use the value of the register, even though the in-memory
        version of the object has been changed.  However, to keep the error
        properly bounded, if the implementation chooses to read the in-memory
        version, it has to be consistent -- it cannot then assume that
        something it has proven about the register is true of the memory
        location.  For example, suppose the formal parameter is L, the value
        of L(6) is now in a register, and L(6) is used in an indexed_
        component as in ``A(L(6)) := 99;'', where A has bounds 1..3.  If the
        implementation can prove that the value for L(6) in the register is
        in the range 1..3, then it need not perform the constraint check if
        it uses the register value.  However, if the memory value of L(6) has
        been changed to 4, and the implementation uses that memory value,
        then it had better not alter memory outside of A.

        12.f   Note that the rule allows the implementation to pass a
        parameter by reference and then keep just part of it in a register,
        or, equivalently, to pass part of the parameter by reference and
        another part by copy.

        12.g   Reason:  We do not want to go so far as to say that the mere
        presence of aliasing is wrong.  We wish to be able to write the
        following sorts of things in standard Ada:

12.h        procedure Move ( Source  : in  String;
                             Target  : out String;
                             Adjust  : in Length_Adjustment :=
                                         (Drop    => Right;
                                          Justify => Left;
                                          Pad     => Representations.Pad ) );
            -- Copies elements from Source to Target (safely if they overlap)

        12.i   This is from the standard string handling package.  It would
        be embarrassing if this couldn't be written in Ada!

        12.j   The ``then'' before ``read'' in the rule implies that the
        implementation can move a read to an earlier place in the code, but
        not to a later place after a potentially aliased assignment.  Thus,
        if the subprogram reads one of its parameters into a local variable,
        and then updates another potentially aliased one, the local copy is
        safe -- it is known to have the old value.  For example, the
        above-mentioned Move subprogram can be implemented by copying Source
        into a local variable before assigning into Target.

        12.k   For an assignment_statement assigning one array parameter to
        another, the implementation has to check which direction to copy at
        run time, in general, in case the actual parameters are overlapping
        slices.  For example:

12.l        procedure Copy(X : in out String; Y: String) is
            begin
                X := Y;
            end Copy;

        12.m   It would be wrong for the compiler to assume that X and Y do
        not overlap (unless, of course, it can prove otherwise).


     NOTES
13   (5) A formal parameter of mode in is a constant view (see 3.3); it
     cannot be updated within the subprogram_body.


                            Extensions to Ada 83

        13.a   {extensions to Ada 83} The value of an out parameter may be
        read.  An out parameter is treated like a declared variable without
        an explicit initial expression.

                         Wording Changes From Ada 83

        13.b   Discussion of copy-in for parts of out parameters is now
        covered in 6.4.1, ``Parameter Associations''.

        13.c   The concept of a by-reference type is new to Ada 9X.

        13.d   We now cover in a general way in 3.7.2 the rule regarding
        erroneous execution when a discriminant is changed and one of the
        parameters depends on the discriminant.



6.3 Subprogram Bodies

1   [A subprogram_body specifies the execution of a subprogram.]


                                   Syntax

2   subprogram_body ::=
        subprogram_specification is
           declarative_part
        begin
            handled_sequence_of_statements
        end [designator];

    3   If a designator appears at the end of a subprogram_body, it shall
    repeat the defining_designator of the subprogram_specification.


                               Legality Rules

4   [In contrast to other bodies,] a subprogram_body need not be the
completion of a previous declaration[, in which case the body declares the
subprogram].  If the body is a completion, it shall be the completion of a
subprogram_declaration or generic_subprogram_declaration.  The profile of a
subprogram_body that completes a declaration shall conform fully to that of
the declaration.  {full conformance (required)}


                              Static Semantics

5   A subprogram_body is considered a declaration.  It can either complete a
previous declaration, or itself be the initial declaration of the subprogram.


                              Dynamic Semantics

6   {elaboration [non-generic subprogram_body]} The elaboration of a
non-generic subprogram_body has no other effect than to establish that the
subprogram can from then on be called without failing the Elaboration_Check.

        6.a   Ramification:  See 12.2 for elaboration of a generic body.
        Note that protected subprogram_bodies never get elaborated; the
        elaboration of the containing protected_body allows them to be called
        without failing the Elaboration_Check.

7   {execution [subprogram_body]} [The execution of a subprogram_body is
invoked by a subprogram call.]  For this execution the declarative_part is
elaborated, and the handled_sequence_of_statements is then executed.


                                  Examples

8   Example of procedure body:

9   procedure Push(E : in Element_Type; S : in out Stack) is
    begin
       if S.Index = S.Size then
          raise Stack_Overflow;
       else
          S.Index := S.Index + 1;
          S.Space(S.Index) := E;
       end if;
    end Push;

10   Example of a function body:

11  function Dot_Product(Left, Right : Vector) return Real is
       Sum : Real := 0.0;
    begin
       Check(Left'First = Right'First and Left'Last = Right'Last);
       for J in Left'Range loop
          Sum := Sum + Left(J)*Right(J);
       end loop;
       return Sum;
    end Dot_Product;


                            Extensions to Ada 83

        11.a   {extensions to Ada 83} A renaming_declaration may be used
        instead of a subprogram_body.

                         Wording Changes From Ada 83

        11.b   The syntax rule for subprogram_body now uses the syntactic
        category handled_sequence_of_statements.

        11.c   The declarative_part of a subprogram_body is now required;
        that doesn't make any real difference, because a declarative_part can
        be empty.

        11.d   We have incorporated some rules from RM83-6.5 here.

        11.e   RM83 forgot to restrict the definition of elaboration of a
        subprogram_body to non-generics.



6.3.1 Conformance Rules

1   {conformance} [When subprogram profiles are given in more than one place,
they are required to conform in one of four ways: type conformance, mode
conformance, subtype conformance, or full conformance.]


                              Static Semantics

2   {convention} {calling convention} [As explained in B.1, ``Interfacing
Pragmas'', a convention can be specified for an entity.  For a callable
entity or access-to-subprogram type, the convention is called the calling
convention.]  The following conventions are defined by the language:

    3  {Ada calling convention} {calling convention (Ada)} The default
       calling convention for any subprogram not listed below is Ada.
       [A pragma Convention, Import, or Export may be used to override
       the default calling convention (see B.1)].

 3.a    Ramification:  See also the rule about renamings-as-body in
        8.5.4.

    4  {Intrinsic calling convention} {calling convention (Intrinsic)}
       The Intrinsic calling convention represents subprograms that are
       ``built in'' to the compiler.  The default calling convention is
       Intrinsic for the following:

           5  an enumeration literal;

           6  a "/=" operator declared implicitly due to the declaration
              of "=" (see 6.6);

           7  any other implicitly declared subprogram unless it is a
              dispatching operation of a tagged type;

           8  an inherited subprogram of a generic formal tagged type
              with unknown discriminants; {94-4774.b}

           9  an attribute that is a subprogram;

          10  a subprogram declared immediately within a protected_body.

       11   [The Access attribute is not allowed for Intrinsic
       subprograms.]  {94-4774.b}

        11.a   Ramification:  The Intrinsic calling convention really
        represents any number of calling conventions at the machine code
        level; the compiler might have a different instruction sequence
        for each intrinsic.  That's why the Access attribute is
        disallowed.  We do not wish to require the implementation to
        generate an out of line body for an intrinsic.

        11.b   Whenever we wish to disallow the Access attribute in
        order to ease implementation, we make the subprogram Intrinsic.
        Several language-defined subprograms have ``pragma
        Convention(Intrinsic, ...);''.  An implementation might actually
        implement this as ``pragma Import(Intrinsic, ...);'', if there
        is really no body, and the implementation of the subprogram is
        built into the code generator.

        11.c   Subprograms declared in protected_bodies will generally
        have a special calling convention so as to pass along the
        identification of the current instance of the protected type.
        The convention is not protected since such local subprograms
        need not contain any ``locking'' logic since they are not
        callable via ``external'' calls; this rule prevents an access
        value designating such a subprogram from being passed outside
        the protected unit.

        11.d   The ``implicitly declared subprogram'' above refers to
        predefined operators (other than the "=" of a tagged type) and
        the inherited subprograms of untagged types.

   12  {protected calling convention} {calling convention (protected)}
       The default calling convention is protected for a protected
       subprogram, and for an access-to-subprogram type with the
       reserved word protected in its definition.

   13  {entry calling convention} {calling convention (entry)} The
       default calling convention is entry for an entry.

14   Of these four conventions, only Ada and Intrinsic are allowed as a
convention_identifier in a pragma Convention, Import, or Export.

        14.a   Discussion:  The names of the protected and entry calling
        conventions cannot be used in the interfacing pragmas.  Note that
        protected and entry are reserved words.

15   {type conformance} {profile (type conformant)} Two profiles are type
conformant if they have the same number of parameters, and both have a result
if either does, and corresponding parameter and result types are the same,
or, for access parameters, corresponding designated types are the same.
{type profile: see profile, type conformant}

        15.a   Discussion:  For access parameters, the designated types have
        to be the same for type conformance, not the access types, since in
        general each access parameter has its own anonymous access type,
        created when the subprogram is called.  Of course, corresponding
        parameters have to be either both access parameters or both not
        access parameters.

16   {mode conformance} {profile (mode conformant)} Two profiles are mode
conformant if they are type-conformant, and corresponding parameters have
identical modes, and, for access parameters, the designated subtypes
statically match.  {statically matching [required]}

17   {subtype conformance} {profile (subtype conformant)} Two profiles are
subtype conformant if they are mode-conformant, corresponding subtypes of the
profile statically match, and the associated calling conventions are the
same.  {94-4774.b} The profile of a generic formal subprogram is not
subtype-conformant with any other profile.  {statically matching [required]}

        17.a   Ramification:  {generic contract issue [partial]}

18   {full conformance (for profiles)} {profile (fully conformant)} Two
profiles are fully conformant if they are subtype-conformant, and
corresponding parameters have the same names and have default_expressions
that are fully conformant with one another.

        18.a   Ramification:  Full conformance requires subtype conformance,
        which requires the same calling conventions.  However, the calling
        convention of the declaration and body of a subprogram or entry are
        always the same by definition.

19   {full conformance (for expressions)} Two expressions are fully
conformant if, [after replacing each use of an operator with the equivalent
function_call:]

   20  each constituent construct of one corresponds to an instance of
       the same syntactic category in the other, except that an expanded
       name may correspond to a direct_name (or character_literal) or to
       a different expanded name in the other; and

   21  each direct_name, character_literal, and selector_name that is
       not part of the prefix of an expanded name in one denotes the
       same declaration as the corresponding direct_name, character_
       literal, or selector_name in the other; and {94-4718.c}
       {94-4752.a}

 21.a   Ramification:  Note that it doesn't say ``respectively'' because
        a direct_name can correspond to a selector_name, and vice-versa,
        by the previous bullet.  This rule allows the prefix of an
        expanded name to be removed, or replaced with a different prefix
        that denotes a renaming of the same entity.  However, it does
        not allow a direct_name or selector_name to be replaced with one
        denoting a distinct renaming (except for direct_names and
        selector_names in prefixes of expanded names).  Note that calls
        using operator notation are equivalent to calls using prefix
        notation.

 21.b   Given the following declarations:

21.c        package A is
                function F(X : Integer := 1) return Boolean;
            end A;

21.d        with A;
            package B is
                package A_View renames A;
                function F_View(X : Integer := 9999) return Boolean renames F;
            end B;

21.e        with A, B; use A, B;
            procedure Main is ...

 21.f   Within Main, the expressions ``F'', ``A.F'', ``B.A_View.F'', and
        ``A_View.F'' are all fully conformant with one another.
        However, ``F'' and ``F_View'' are not fully conformant.  If they
        were, it would be bad news, since the two denoted views have
        different default_expressions.

   22  each primary that is a literal in one has the same value as the
       corresponding literal in the other.

 22.a   Ramification:  The literals may be written differently.

        22.b   Ramification:  Note that the above definition makes full
        conformance a transitive relation.

23   {full conformance (for known_discriminant_parts)} Two known_
discriminant_parts are fully conformant if they have the same number of
discriminants, and discriminants in the same positions have the same names,
statically matching subtypes, and default_expressions that are fully
conformant with one another.  {statically matching [required]}

24   {full conformance (for discrete_subtype_definitions)} Two discrete_
subtype_definitions are fully conformant if they are both subtype_indications
or are both ranges, the subtype_marks (if any) denote the same subtype, and
the corresponding simple_expressions of the ranges (if any) fully conform.

        24.a   Ramification:  In the subtype_indication case, any ranges have
        to be corresponding; that is, two subtype_indications cannot conform
        unless both or neither has a range.

        24.b   Discussion:  This definition is used in 9.5.2, ``Entries and
        Accept Statements'' for the conformance required between the
        discrete_subtype_definitions of an entry_declaration for a family of
        entries and the corresponding entry_index_specification of the entry_
        body.


                         Implementation Permissions

25   An implementation may declare an operator declared in a language-defined
library unit to be intrinsic.


                            Extensions to Ada 83

        25.a   {extensions to Ada 83} The rules for full conformance are
        relaxed -- they are now based on the structure of constructs, rather
        than the sequence of lexical elements.  This implies, for example,
        that "(X, Y: T)" conforms fully with "(X: T; Y: T)", and "(X: T)"
        conforms fully with "(X: in T)".  {94-4718.c}



6.3.2 Inline Expansion of Subprograms

1   [Subprograms may be expanded in line at the call site.]


                                   Syntax

    2   {program unit pragma [Inline]} {pragma, program unit [Inline]} The
    form of a pragma Inline, which is a program unit pragma (see 10.1.5), is
    as follows:


3     pragma Inline(name {, name});


                               Legality Rules

4   The pragma shall apply to one or more callable entities or generic
subprograms.


                              Static Semantics

5   If a pragma Inline applies to a callable entity, this indicates that
inline expansion is desired for all calls to that entity.  If a pragma Inline
applies to a generic subprogram, this indicates that inline expansion is
desired for all calls to all instances of that generic subprogram.

        5.a   Ramification:  Note that inline expansion is desired no matter
        what name is used in the call.  This allows one to request inlining
        for only one of several overloaded subprograms as follows:

5.b         package IO is
               procedure Put(X : in Integer);
               procedure Put(X : in String);
               procedure Put(X : in Character);
            private
               procedure Character_Put(X : in Character) renames Put;
               pragma Inline(Character_Put);
            end IO;

5.c         with IO; use IO;
            procedure Main is
               I : Integer;
               C : Character;
            begin
               ...
               Put(C); -- Inline expansion is desired.
               Put(I); -- Inline expansion is NOT desired.
            end Main;

        5.d   Ramification:  The meaning of a subprogram can be changed by a
        pragma Inline only in the presence of failing checks (see 11.6).
                         Implementation Permissions

6   For each call, an implementation is free to follow or to ignore the
recommendation expressed by the pragma.

        6.a   Ramification:  Note, in particular, that the recommendation
        cannot always be followed for a recursive call, and is often
        infeasible for entries.  Note also that the implementation can inline
        calls even when no such desire was expressed by a pragma, so long as
        the semantics of the program remains unchanged.  {94-4477.a}


     NOTES
7    (6) The name in a pragma Inline can denote more than one entity in the
     case of overloading.  Such a pragma applies to all of the denoted
     entities.


                            Extensions to Ada 83

        7.a   {extensions to Ada 83} A pragma Inline is allowed inside a
        subprogram_body if there is no corresponding subprogram_declaration.
        This is for uniformity with other program unit pragmas.



6.4 Subprogram Calls

1   {subprogram call} A subprogram call is either a procedure_call_statement
or a function_call; [it invokes the execution of the subprogram_body.  The
call specifies the association of the actual parameters, if any, with formal
parameters of the subprogram.]


                                   Syntax

2   procedure_call_statement ::=
        procedure_name;
      | procedure_prefix actual_parameter_part;

3   function_call ::=
        function_name
      | function_prefix actual_parameter_part

4   actual_parameter_part ::=
        (parameter_association {, parameter_association})

5   parameter_association ::=
       [formal_parameter_selector_name =>] explicit_actual_parameter

6   explicit_actual_parameter ::= expression | variable_name

    7   {named association} {positional association} A parameter_association
    is named or positional according to whether or not the formal_
    parameter_selector_name is specified.  Any positional associations shall
    precede any named associations.  Named associations are not allowed if
    the prefix in a subprogram call is an attribute_reference.

        7.a   Ramification:  This means that the formal parameter names used
        in describing predefined attributes are to aid presentation of their
        semantics, but are not intended for use in actual calls.


                            Name Resolution Rules

8   The name or prefix given in a procedure_call_statement shall resolve to
denote a callable entity that is a procedure, or an entry renamed as (viewed
as) a procedure.  The name or prefix given in a function_call shall resolve
to denote a callable entity that is a function.  [When there is an actual_
parameter_part, the prefix can be an implicit_dereference of an
access-to-subprogram value.]

        8.a   Ramification:  The function can be an operator, enumeration
        literal, attribute that is a function, etc.

9   A subprogram call shall contain at most one association for each formal
parameter.  Each formal parameter without an association shall have a
default_expression (in the profile of the view denoted by the name or
prefix).  This rule is an overloading rule (see 8.6).


                              Dynamic Semantics

10   {execution [subprogram call]} For the execution of a subprogram call,
the name or prefix of the call is evaluated, and each parameter_association
is evaluated (see 6.4.1).  If a default_expression is used, an implicit
parameter_association is assumed for this rule.  These evaluations are done
in an arbitrary order.  The subprogram_body is then executed.  Finally, if
the subprogram completes normally, then after it is left, any necessary
assigning back of formal to actual parameters occurs (see 6.4.1).

        10.a   Discussion:  The implicit association for a default is only
        for this run-time rule.  At compile time, the visibility rules are
        applied to the default at the place where it occurs, not at the place
        of a call.

        10.b   To be honest:  If the subprogram is inherited, see 3.4,
        ``Derived Types and Classes''.

        10.c   If the subprogram is protected, see 9.5.1, ``Protected
        Subprograms and Protected Actions''.

        10.d   If the subprogram is really a renaming of an entry, see 9.5.3,
        ``Entry Calls''.

        10.e   Normally, the subprogram_body that is executed by the above
        rule is the one for the subprogram being called.  For an enumeration
        literal, implicitly declared (but noninherited) subprogram, or an
        attribute that is a subprogram, an implicit body is assumed.  For a
        dispatching call, 3.9.2, ``Dispatching Operations of Tagged Types''
        defines which subprogram_body is executed.

11   {Program_Error (raised by failure of run-time check)} The exception
Program_Error is raised at the point of a function_call if the function
completes normally without executing a return_statement.

        11.a   Discussion:  We are committing to raising the exception at the
        point of call, for uniformity -- see AI-00152.  This happens after
        the function is left, of course.

        11.b   Note that there is no name for suppressing this check, since
        the check imposes no time overhead and minimal space overhead (since
        it can usually be statically eliminated as dead code).

12   A function_call denotes a constant, as defined in 6.5; the nominal
subtype of the constant is given by the result subtype of the function.
{nominal subtype [of the result of a function_call]} {constant [result of a
function_call]}


                                  Examples

13   Examples of procedure calls:

14  Traverse_Tree;                                               --  see 6.1
    Print_Header(128, Title, True);                              --  see 6.1

15  Switch(From => X, To => Next);                               --  see 6.1
    Print_Header(128, Header => Title, Center => True);          --  see 6.1
    Print_Header(Header => Title, Center => True, Pages => 128); --  see 6.1

16   Examples of function calls:

17  Dot_Product(U, V)   --  see 6.1 and 6.3
    Clock               --  see 9.6
    F.all               --  presuming F is of an access-to-subprogram type -- s\
ee 3.10

18   Examples of procedures with default expressions:

19  procedure Activate(Process : in Process_Name;
                       After   : in Process_Name := No_Process;
                       Wait    : in Duration := 0.0;
                       Prior   : in Boolean := False);

20  procedure Pair(Left, Right : in Person_Name := new Person);   --  see 3.10.1

21   Examples of their calls:

22  Activate(X);
    Activate(X, After => Y);
    Activate(X, Wait => 60.0, Prior => True);
    Activate(X, Y, 10.0, False);

23  Pair;
    Pair(Left => new Person, Right => new Person);


     NOTES
24   (7) If a default_expression is used for two or more parameters in a
     multiple parameter_specification, the default_expression is evaluated
     once for each omitted parameter.  Hence in the above examples, the two
     calls of Pair are equivalent.


                                  Examples

25   Examples of overloaded subprograms:

26  procedure Put(X : in Integer);
    procedure Put(X : in String);

27  procedure Set(Tint   : in Color);
    procedure Set(Signal : in Light);

28   Examples of their calls:

29  Put(28);
    Put("no possible ambiguity here");

30  Set(Tint   => Red);
    Set(Signal => Red);
    Set(Color'(Red));

31  --  Set(Red) would be ambiguous since Red may
    --  denote a value either of type Color or of type Light


                         Wording Changes From Ada 83
        31.a   We have gotten rid of parameters ``of the form of a type
        conversion'' (see RM83-6.4.1(3)).  The new view semantics of type_
        conversions allows us to use normal type_conversions instead.

        31.b   We have moved wording about run-time semantics of parameter
        associations to 6.4.1.

        31.c   We have moved wording about raising Program_Error for a
        function that falls off the end to here from RM83-6.5.



6.4.1 Parameter Associations

1   [{parameter passing} A parameter association defines the association
between an actual parameter and a formal parameter.]


                         Language Design Principles

        1.a   The parameter passing rules for out parameters are designed to
        ensure that the parts of a type that have implicit initial values
        (see 3.3.1) don't become ``de-initialized'' by being passed as an out
        parameter.

                            Name Resolution Rules

2   The formal_parameter_selector_name of a parameter_association shall
resolve to denote a parameter_specification of the view being called.

3   {actual parameter (for a formal parameter)} The actual parameter is
either the explicit_actual_parameter given in a parameter_association for a
given formal parameter, or the corresponding default_expression if no
parameter_association is given for the formal parameter.  {expected type
(actual parameter)} The expected type for an actual parameter is the type of
the corresponding formal parameter.

        3.a   To be honest:  The corresponding default_expression is the one
        of the corresponding formal parameter in the profile of the view
        denoted by the name or prefix of the call.

4   If the mode is in, the actual is interpreted as an expression; otherwise,
the actual is interpreted only as a name, if possible.

        4.a   Ramification:  This formally resolves the ambiguity present in
        the syntax rule for explicit_actual_parameter.  Note that we don't
        actually require that the actual be a name if the mode is not in; we
        do that below.


                               Legality Rules

5   If the mode is in out or out, the actual shall be a name that denotes a
variable.

        5.a   Discussion:  We no longer need ``or a type_conversion whose
        argument is the name of a variable,'' because a type_conversion is
        now a name, and a type_conversion of a variable is a variable.

        5.b   Reason:  The requirement that the actual be a (variable) name
        is not an overload resolution rule, since we don't want the
        difference between expression and name to be used to resolve
        overloading.  For example:

5.c         procedure Print(X : in Integer; Y : in Boolean := True);
            procedure Print(Z : in out Integer);
            . . .
            Print(3); -- Ambiguous!

        5.d   The above call to Print is ambiguous even though the call is
        not compatible with the second Print which requires an actual that is
        a (variable) name (``3'' is an expression, not a name).  This
        requirement is a legality rule, so overload resolution fails before
        it is considered, meaning that the call is ambiguous.

6   The type of the actual parameter associated with an access parameter
shall be convertible (see 4.6) to its anonymous access type.  {convertible
[required]}


                              Dynamic Semantics

7   {evaluation [parameter_association]} For the evaluation of a parameter_
association:

    8  The actual parameter is first evaluated.

    9  For an access parameter, the access_definition is elaborated,
       which creates the anonymous access type.

   10  For a parameter [(of any mode)] that is passed by reference (see
       6.2), a view conversion of the actual parameter to the nominal
       subtype of the formal parameter is evaluated, and the formal
       parameter denotes that conversion.  {implicit subtype conversion
       [parameter passing]}

 10.a   Discussion:  We are always allowing sliding, even for [in] out
        by-reference parameters.

   11  {assignment operation (during evaluation of a parameter_
       association)} For an in or in out parameter that is passed by
       copy (see 6.2), the formal parameter object is created, and the
       value of the actual parameter is converted to the nominal subtype
       of the formal parameter and assigned to the formal.  {implicit
       subtype conversion [parameter passing]}

 11.a   Ramification:  The conversion mentioned here is a value
        conversion.

   12  For an out parameter that is passed by copy, the formal parameter
       object is created, and:

          13  For an access type, the formal parameter is initialized
              from the value of the actual, without a constraint check;

 13.a   Reason:  This preserves the Language Design Principle that an
        object of an access type is always initialized with a
        ``reasonable'' value.

          14  For a composite type with discriminants or that has
              implicit initial values for any subcomponents (see 3.3.1),
              the behavior is as for an in out parameter passed by copy.
              {94-4783.a} {94-4785.a}

 14.a   Reason:  This ensures that no part of an object of such a type
        can become ``de-initialized'' by being part of an out parameter.
        {94-4783.b}

 14.b   Ramification:  This includes an array type whose component type
        is an access type, and a record type with a component that has a
        default_expression, among other things.

          15  For any other type, the formal parameter is uninitialized.
              If composite, a view conversion of the actual parameter to
              the nominal subtype of the formal is evaluated [(which
              might raise Constraint_Error)], and the actual subtype of
              the formal is that of the view conversion.  If elementary,
              the actual subtype of the formal is given by its nominal
              subtype.

 15.a   Ramification:  This case covers scalar types, and composite
        types whose subcomponent's subtypes do not have any implicit
        initial values.  The view conversion for composite types ensures
        that if the lengths don't match between an actual and a formal
        array parameter, the Constraint_Error is raised before the call,
        rather than after.

16   {constrained [object]} {unconstrained [object]} A formal parameter of
mode in out or out with discriminants is constrained if either its nominal
subtype or the actual parameter is constrained.

17   {parameter copy back} {copy back of parameters} {parameter assigning
back} {assigning back of parameters} {assignment operation (during parameter
copy back)} After normal completion and leaving of a subprogram, for each in
out or out parameter that is passed by copy, the value of the formal
parameter is converted to the subtype of the variable given as the actual
parameter and assigned to it.  {implicit subtype conversion [parameter
passing]} These conversions and assignments occur in an arbitrary order.

        17.a   Ramification:  The conversions mentioned above during
        parameter passing might raise Constraint_Error -- (see 4.6).

        17.b   Ramification:  If any conversion or assignment as part of
        parameter passing propagates an exception, the exception is raised at
        the place of the subprogram call; that is, it cannot be handled
        inside the subprogram_body.

        17.c   Proof:  Since these checks happen before or after executing
        the subprogram_body, the execution of the subprogram_body does not
        dynamically enclose them, so it can't handle the exceptions.

        17.d   Discussion:  The variable we're talking about is the one
        denoted by the variable_name given as the explicit_actual_parameter.
        If this variable_name is a type_conversion, then the rules in 4.6 for
        assigning to a view conversion apply.  That is, if X is of subtype
        S1, and the actual is S2(X), the above-mentioned conversion will
        convert to S2, and the one mentioned in 4.6 will convert to S1.


                            Extensions to Ada 83

        17.e   {extensions to Ada 83} In Ada 9X, a program can rely on the
        fact that passing an object as an out parameter does not
        ``de-initialize'' any parts of the object whose subtypes have
        implicit initial values.  (This generalizes the RM83 rule that
        required copy-in for parts that were discriminants or of an access
        type.)

                         Wording Changes From Ada 83

        17.f   We have eliminated the subclause on Default Parameters, as it
        is subsumed by earlier clauses and subclauses.



6.5 Return Statements

1   A return_statement is used to complete the execution of the innermost
enclosing subprogram_body, entry_body, or accept_statement.
                                   Syntax

2   return_statement ::= return [expression];


                            Name Resolution Rules

3   {return expression} The expression, if any, of a return_statement is
called the return expression.  {result subtype (of a function)} The result
subtype of a function is the subtype denoted by the subtype_mark after the
reserved word return in the profile of the function.  {expected type [return
expression]} The expected type for a return expression is the result type of
the corresponding function.

        3.a   To be honest:  The same applies to generic functions.


                               Legality Rules

4   {apply (to a callable construct by a return_statement)} A return_
statement shall be within a callable construct, and it applies to the
innermost one.  A return_statement shall not be within a body that is within
the construct to which the return_statement applies.

5   A function body shall contain at least one return_statement that applies
to the function body, unless the function contains code_statements.  A
return_statement shall include a return expression if and only if it applies
to a function body.

        5.a   Reason:  The requirement that a function body has to have at
        least one return_statement is a ``helpful'' restriction.  There was
        been some interest in lifting this restriction, or allowing a raise
        statement to substitute for the return_statement.  However, there was
        enough interest in leaving it as is that we decided not to change it.


                              Dynamic Semantics

6   {execution [return_statement]} For the execution of a return_statement,
the expression (if any) is first evaluated and converted to the result
subtype.  {implicit subtype conversion [function return]}

        6.a   Ramification:  The conversion might raise Constraint_Error --
        (see 4.6).

7   If the result type is class-wide, then the tag of the result is the tag
of the value of the expression.

8   If the result type is a specific tagged type:

    9  {Tag_Check [partial]} {check, language-defined (Tag_Check)} If it
       is limited, then a check is made that the tag of the value of the
       return expression identifies the result type.  {Constraint_Error
       (raised by failure of run-time check)} Constraint_Error is raised
       if this check fails.

   10  If it is nonlimited, then the tag of the result is that of the
       result type.

 10.a   Ramification:  This is true even if the tag of the return
        expression is different.

 10.b   Reason:  These rules ensure that a function whose result type is
        a specific tagged type always returns an object whose tag is
        that of the result type.  This is important for dispatching on
        controlling result, and, if nonlimited, allows the caller to
        allocate the appropriate amount of space to hold the value being
        returned (assuming there are no discriminants).

11   {return-by-reference type} A type is a return-by-reference type if it is
a descendant of one of the following:

   12  a tagged limited type;

   13  a task or protected type;

   14  a nonprivate type with the reserved word limited in its
       declaration;

   15  a composite type with a subcomponent of a return-by-reference
       type;

   16  a private type whose full type is a return-by-reference type.

        16.a   Ramification:  The above rules are such that there are no "Ada
        83" types other than those containing tasks that are return-by-
        reference.  This helps to minimize upward incompatibilities relating
        to return-by-reference.

17   {Accessibility_Check [partial]} {check, language-defined (Accessibility_
Check)} If the result type is a return-by-reference type, then a check is
made that the return expression is one of the following:

   18  a name that denotes an object view whose accessibility level is
       not deeper than that of the master that elaborated the function
       body; or

   19  a parenthesized expression or qualified_expression whose operand
       is one of these kinds of expressions.  {94-4715.a}

20   {Program_Error (raised by failure of run-time check)} The exception
Program_Error is raised if this check fails.

        20.a   Discussion:  Compare the definition of return-by-reference
        with that of by-reference.

        20.b   The return-by-reference types are all limited types except
        those that are limited only because of a limited private type with a
        nonlimited untagged full type.

        20.c   Reason:  {generic contract issue [partial]}

        20.d   This check can often be performed at compile time.  It is
        defined to be a run-time check to avoid generic contract model
        problems.  In a future version of the standard, we anticipate that
        function return of a local variable will be illegal for all limited
        types, eliminating the need for the run-time check except for
        dereferences of an access parameter.

21   For a function with a return-by-reference result type the result is
returned by reference; that is, the function call denotes a constant view of
the object associated with the value of the return expression.  {assignment
operation (during execution of a return_statement)} For any other function,
the result is returned by copy; that is, the converted value is assigned into
an anonymous constant created at the point of the return_statement, and the
function call denotes that object.

        21.a   Ramification:  The assignment operation does the necessary
        value adjustment, as described in 7.6, ``User-Defined Assignment and
        Finalization''.  7.6.1 describes when the anonymous constant is
        finalized.

22   Finally, a transfer of control is performed which completes the
execution of the callable construct to which the return_statement applies,
and returns to the caller.


                                  Examples

23   Examples of return statements:

24  return;                         -- in a procedure body, entry_body, or acce\
pt_statement
    return Key_Value(Last_Index);   -- in a function body


                        Incompatibilities With Ada 83

        24.a   {incompatibilities with Ada 83} In Ada 9X, if the result type
        of a function has a part that is a task, then an attempt to return a
        local variable will raise Program_Error.  In Ada 83, if a function
        returns a local variable containing a task, execution is erroneous
        according to AI-00867.  However, there are other situations where
        functions that return tasks (or that return a variant record only one
        of whose variants includes a task) are correct in Ada 83 but will
        raise Program_Error according to the new rules.

        24.b   The rule change was made because there will be more types
        (protected types, limited controlled types) in Ada 9X for which it
        will be meaningless to return a local variable, and making all of
        these erroneous is unacceptable.  The current rule was felt to be the
        simplest that kept upward incompatibilities to situations involving
        returning tasks, which are quite rare.

                         Wording Changes From Ada 83

        24.c   This clause has been moved here from chapter 5, since it has
        mainly to do with subprograms.

        24.d   A function now creates an anonymous object.  This is necessary
        so that controlled types will work.

        24.e   We have clarified that a return_statement applies to a
        callable construct, not to a callable entity.

        24.f   There is no need to mention generics in the rules about where
        a return_statement can appear and what it applies to; the phrase
        ``body of a subprogram or generic subprogram'' is syntactic, and
        refers exactly to ``subprogram_body''.



6.6 Overloading of Operators

1   {operator} {user-defined operator} {operator (user-defined)} An operator
is a function whose designator is an operator_symbol.  [Operators, like other
functions, may be overloaded.]


                            Name Resolution Rules

2   Each use of a unary or binary operator is equivalent to a function_call
with function_prefix being the corresponding operator_symbol, and with
(respectively) one or two positional actual parameters being the operand(s)
of the operator (in order).

        2.a   To be honest:  We also use the term operator (in Section 4 and
        in 6.1) to refer to one of the syntactic categories defined in 4.5,
        ``Operators and Expression Evaluation'' whose names end with
        ``_operator:''  logical_operator, relational_operator, binary_adding_
        operator, unary_adding_operator, multiplying_operator, and highest_
        precedence_operator.


                               Legality Rules

3   The subprogram_specification of a unary or binary operator shall have one
or two parameters, respectively.  A generic function instantiation whose
designator is an operator_symbol is only allowed if the specification of the
generic function has the corresponding number of parameters.

4   Default_expressions are not allowed for the parameters of an operator
(whether the operator is declared with an explicit subprogram_specification
or by a generic_instantiation).

5   An explicit declaration of "/=" shall not have a result type of the
predefined type Boolean.


                              Static Semantics

6   A declaration of "=" whose result type is Boolean implicitly declares a
declaration of "/=" that gives the complementary result.  {94-4701.a}


     NOTES
7    (8) The operators "+" and "-" are both unary and binary operators, and
     hence may be overloaded with both one- and two-parameter functions.


                                  Examples

8   Examples of user-defined operators:

9   function "+" (Left, Right : Matrix) return Matrix;
    function "+" (Left, Right : Vector) return Vector;

    --  assuming that A, B, and C are of the type Vector
    --  the following two statements are equivalent:

    A := B + C;
    A := "+"(B, C);


                            Extensions to Ada 83

        9.a   {extensions to Ada 83} Explicit declarations of "=" are now
        permitted for any combination of parameter and result types.

        9.b   Explicit declarations of "/=" are now permitted, so long as the
        result type is not Boolean.



                             Section 7: Packages


1   [{Package} [glossary entry]Packages are program units that allow the
specification of groups of logically related entities.  Typically, a package
contains the declaration of a type (often a private type or private
extension) along with the declarations of primitive subprograms of the type,
which can be called from outside the package, while their inner workings
remain hidden from outside users.{information hiding: see package}
{encapsulation: see package} {module: see package} {class: see also package}]



7.1 Package Specifications and Declarations

1   [A package is generally provided in two parts: a package_specification
and a package_body.  Every package has a package_specification, but not all
packages have a package_body.]


                                   Syntax

2   package_declaration ::= package_specification;

3   package_specification ::=
        package defining_program_unit_name is
          {basic_declarative_item}
       [private
          {basic_declarative_item}]
        end [[parent_unit_name.]identifier]

    4   If an identifier or parent_unit_name.identifier appears at the end of
    a package_specification, then this sequence of lexical elements shall
    repeat the defining_program_unit_name.


                               Legality Rules

5   {requires a completion [package_declaration]} {requires a completion
[generic_package_declaration]} A package_declaration or generic_package_
declaration requires a completion [(a body)] if it contains any declarative_
item that requires a completion, but whose completion is not in its package_
specification.

        5.a   To be honest:  If an implementation supports it, a pragma
        Import may substitute for the body of a package or generic package.


                              Static Semantics

6   {visible part [of a package (other than a generic formal package)]} The
first list of declarative_items of a package_specification of a package other
than a generic formal package is called the visible part of the package.
[{private part [of a package]} The optional list of declarative_items after
the reserved word private (of any package_specification) is called the
private part of the package.  If the reserved word private does not appear,
the package has an implicit empty private part.]

        6.a   Ramification:  This definition of visible part does not apply
        to generic formal packages -- 12.7 defines the visible part of a
        generic formal package.

        6.b   The implicit empty private part is important because certain
        implicit declarations occur there if the package is a child package,
        and it defines types in its visible part that are derived from, or
        contain as components, private types declared within the parent
        package.  These implicit declarations are visible in children of the
        child package.  See 10.1.1.

7   [An entity declared in the private part of a package is visible only
within the declarative region of the package itself (including any child
units -- see 10.1.1).  In contrast, expanded names denoting entities declared
in the visible part can be used even outside the package; furthermore, direct
visibility of such entities can be achieved by means of use_clauses (see
4.1.3 and 8.4).]


                              Dynamic Semantics

8   {elaboration [package_declaration]} The elaboration of a package_
declaration consists of the elaboration of its basic_declarative_items in the
given order.


     NOTES
9    (1) The visible part of a package contains all the information that
     another program unit is able to know about the package.

10   (2) If a declaration occurs immediately within the specification of a
     package, and the declaration has a corresponding completion that is a
     body, then that body has to occur immediately within the body of the
     package.

   10.a   Proof:  This follows from the fact that the declaration and
        completion are required to occur immediately within the same
        declarative region, and the fact that bodies are disallowed (by the
        Syntax Rules) in package_specifications.  This does not apply to
        instances of generic units, whose bodies can occur in package_
        specifications.


                                  Examples

11   Example of a package declaration:

12  package Rational_Numbers is

13     type Rational is
          record
             Numerator   : Integer;
             Denominator : Positive;
          end record;

14     function "="(X,Y : Rational) return Boolean;

15     function "/"  (X,Y : Integer)  return Rational;  --  to construct a rati\
onal number

16     function "+"  (X,Y : Rational) return Rational;
       function "-"  (X,Y : Rational) return Rational;
       function "*"  (X,Y : Rational) return Rational;
       function "/"  (X,Y : Rational) return Rational;
    end Rational_Numbers;

17   There are also many examples of package declarations in the predefined
language environment (see Annex A).


                        Incompatibilities With Ada 83

        17.a   {incompatibilities with Ada 83} In Ada 83, a library package
        is allowed to have a body even if it doesn't need one.  In Ada 9X, a
        library package body is either required or forbidden -- never
        optional.  The workaround is to add pragma Elaborate_Body, or
        something else requiring a body, to each library package that has a
        body that isn't otherwise required.

                         Wording Changes From Ada 83

        17.b   We have moved the syntax into this clause and the next clause
        from RM83-7.1, ``Package Structure'', which we have removed.

        17.c   RM83 was unclear on the rules about when a package requires a
        body.  For example, RM83-7.1(4) and RM83-7.1(8) clearly forgot about
        the case of an incomplete type declared in a package_declaration but
        completed in the body.  In addition, RM83 forgot to make this rule
        apply to a generic package.  We have corrected these rules.  Finally,
        since we now allow a pragma Import for any explicit declaration, the
        completion rules need to take this into account as well.



7.2 Package Bodies

1   [In contrast to the entities declared in the visible part of a package,
the entities declared in the package_body are visible only within the
package_body itself.  As a consequence, a package with a package_body can be
used for the construction of a group of related subprograms in which the
logical operations available to clients are clearly isolated from the
internal entities.]


                                   Syntax

2   package_body ::=
        package body defining_program_unit_name is
           declarative_part
       [begin
            handled_sequence_of_statements]
        end [[parent_unit_name.]identifier];

    3   If an identifier or parent_unit_name.identifier appears at the end of
    a package_body, then this sequence of lexical elements shall repeat the
    defining_program_unit_name.


                               Legality Rules

4   A package_body shall be the completion of a previous package_declaration
or generic_package_declaration.  A library package_declaration or library
generic_package_declaration shall not have a body unless it requires a body[;
pragma Elaborate_Body can be used to require a library_unit_declaration to
have a body (see 10.2.1) if it would not otherwise require one].  {94-4409.a}

        4.a   Ramification:  The first part of the rule forbids a package_
        body from standing alone -- it has to belong to some previous
        package_declaration or generic_package_declaration.

        4.b   A nonlibrary package_declaration or nonlibrary generic_package_
        declaration that does not require a completion may have a
        corresponding body anyway.


                              Static Semantics

5   In any package_body without statements there is an implicit null_
statement.  For any package_declaration without an explicit completion, there
is an implicit package_body containing a single null_statement.  For a
noninstance, nonlibrary package, this body occurs at the end of the
declarative_part of the innermost enclosing program unit or block_statement;
if there are several such packages, the order of the implicit package_bodies
is unspecified.  {unspecified [partial]} [(For an instance, the implicit
package_body occurs at the place of the instantiation (see 12.3).  For a
library package, the place is partially determined by the elaboration
dependences (see Section 10).)]

        5.a   Discussion:  Thus, for example, we can refer to something
        happening just after the begin of a package_body, and we can refer to
        the handled_sequence_of_statements of a package_body, without
        worrying about all the optional pieces.  The place of the implicit
        body makes a difference for tasks activated by the package.  See also
        RM83-9.3(5).

        5.b   The implicit body would be illegal if explicit in the case of a
        library package that does not require (and therefore does not allow)
        a body.  This is a bit strange, but not harmful.


                              Dynamic Semantics

6   {elaboration [nongeneric package_body]} For the elaboration of a
nongeneric package_body, its declarative_part is first elaborated, and its
handled_sequence_of_statements is then executed.


     NOTES
7    (3) A variable declared in the body of a package is only visible within
     this body and, consequently, its value can only be changed within the
     package_body.  In the absence of local tasks, the value of such a
     variable remains unchanged between calls issued from outside the package
     to subprograms declared in the visible part.  The properties of such a
     variable are similar to those of a ``static'' variable of C.

8    (4) The elaboration of the body of a subprogram explicitly declared in
     the visible part of a package is caused by the elaboration of the body
     of the package.  Hence a call of such a subprogram by an outside program
     unit raises the exception Program_Error if the call takes place before
     the elaboration of the package_body (see 3.11).


                                  Examples

9   Example of a package body (see 7.1):

10  package body Rational_Numbers is

11     procedure Same_Denominator (X,Y : in out Rational) is
       begin
          --  reduces X and Y to the same denominator:
          ...
       end Same_Denominator;

12     function "="(X,Y : Rational) return Boolean is
          U : Rational := X;
          V : Rational := Y;
       begin
          Same_Denominator (U,V);
          return U.Numerator = V.Numerator;
       end "=";

13     function "/" (X,Y : Integer) return Rational is
       begin
          if Y > 0 then
             return (Numerator => X,  Denominator => Y);
          else
             return (Numerator => -X, Denominator => -Y);
          end if;
       end "/";

14     function "+" (X,Y : Rational) return Rational is ...  end "+";
       function "-" (X,Y : Rational) return Rational is ...  end "-";
       function "*" (X,Y : Rational) return Rational is ...  end "*";
       function "/" (X,Y : Rational) return Rational is ...  end "/";

15  end Rational_Numbers;


                         Wording Changes From Ada 83

        15.a   The syntax rule for package_body now uses the syntactic
        category handled_sequence_of_statements.

        15.b   The declarative_part of a package_body is now required; that
        doesn't make any real difference, since a declarative_part can be
        empty.

        15.c   RM83 seems to have forgotten to say that a package_body can't
        stand alone, without a previous declaration.  We state that rule
        here.

        15.d   RM83 forgot to restrict the definition of elaboration of
        package_bodies to nongeneric ones.  We have corrected that omission.

        15.e   The rule about implicit bodies (from RM83-9.3(5)) is moved
        here, since it is more generally applicable.



7.3 Private Types and Private Extensions

1   [The declaration (in the visible part of a package) of a type as a
private type or private extension serves to separate the characteristics that
can be used directly by outside program units (that is, the logical
properties) from other characteristics whose direct use is confined to the
package (the details of the definition of the type itself).  See 3.9.1 for an
overview of type extensions.  {private types and private extensions}
{information hiding: see private types and private extensions} {opaque type:
see private types and private extensions} {abstract data type (ADT): see
private types and private extensions} {ADT (abstract data type): see private
types and private extensions}]


                         Language Design Principles

        1.a   A private (untagged) type can be thought of as a record type
        with the type of its single (hidden) component being the full view.

        1.b   A private tagged type can be thought of as a private extension
        of an anonymous parent with no components.  The only dispatching
        operation of the parent is equality (although the Size attribute,
        and, if nonlimited, assignment are allowed, and those will presumably
        be implemented in terms of dispatching).

                                   Syntax

2   private_type_declaration ::=
       type defining_identifier [discriminant_part] is [[abstract] tagged] [lim\
ited] private;

3   private_extension_declaration ::=
       type defining_identifier [discriminant_part] is
         [abstract] new ancestor_subtype_indication with private;


                               Legality Rules

4   {partial view (of a type)} {requires a completion [declaration of a
partial view]} A private_type_declaration or private_extension_declaration
declares a partial view of the type; such a declaration is allowed only as a
declarative_item of the visible part of a package, and it requires a
completion, which shall be a full_type_declaration that occurs as a
declarative_item of the private part of the package.  {full view (of a type)}
The view of the type declared by the full_type_declaration is called the full
view.  A generic formal private type or a generic formal private extension is
also a partial view.

        4.a   To be honest:  A private type can also be completed by a pragma
        Import, if supported by an implementation.
        4.b   Reason:  We originally used the term ``private view,'' but this
        was easily confused with the view provided from the private part,
        namely the full view.

5   [A type shall be completely defined before it is frozen (see 3.11.1 and
13.14).  Thus, neither the declaration of a variable of a partial view of a
type, nor the creation by an allocator of an object of the partial view are
allowed before the full declaration of the type.  Similarly, before the full
declaration, the name of the partial view cannot be used in a generic_
instantiation or in a representation item.]

        5.a   Proof:  This rule is stated officially in 3.11.1, ``Completions
        of Declarations''.

        5.b   Change:  Rule moved here from 13.14, ``Freezing Rules'', as per
        WG9 resolution.

6   [A private type is limited if its declaration includes the reserved word
limited; a private extension is limited if its ancestor type is limited.]  If
the partial view is nonlimited, then the full view shall be nonlimited.  If a
tagged partial view is limited, then the full view shall be limited.  [On the
other hand, if an untagged partial view is limited, the full view may be
limited or nonlimited.]  {94-4662.a} {94-4665.a} {94-4828.b}

7   If the partial view is tagged, then the full view shall be tagged.  [On
the other hand, if the partial view is untagged, then the full view may be
tagged or untagged.]  In the case where the partial view is untagged and the
full view is tagged, no derivatives of the partial view are allowed within
the immediate scope of the partial view; [derivatives of the full view are
allowed.]

        7.a   Ramification:  Note that deriving from a partial view within
        its immediate scope can only occur in a package that is a child of
        the one where the partial view is declared.  The rule implies that in
        the visible part of a public child package, it is impossible to
        derive from an untagged private type declared in the visible part of
        the parent package in the case where the full view of the parent type
        turns out to be tagged.  {94-4443.a} We considered a model in which
        the derived type was implicitly redeclared at the earliest place
        within its immediate scope where characteristics needed to be added.
        However, we rejected that model, because (1) it would imply that (for
        an untagged type) subprograms explicitly declared after the derived
        type could be inherited, and (2) to make this model work for
        composite types as well, several implicit redeclarations would be
        needed, since new characteristics can become visible one by one; that
        seemed like too much mechanism.

        7.b   Discussion:  The rule for tagged partial views is redundant for
        partial views that are private extensions, since all extensions of a
        given ancestor tagged type are tagged, and limited if the ancestor is
        limited.  We phrase this rule partially redundantly to keep its
        structure parallel with the other rules.

        7.c   To be honest:  This rule is checked in a generic unit, rather
        than using the ``assume the best'' or ``assume the worst'' method.

        7.d   Reason:  Tagged limited private types have certain capabilities
        that are incompatible with having assignment for the full view of the
        type.  In particular, tagged limited private types can be extended
        with access discriminants and components of a limited type, which
        works only because assignment is not allowed.  Consider the following
        example:

7.e         package P1 is
                type T1 is tagged limited private;
                procedure Foo(X : in T1'Class);
            private
                type T1 is tagged null record; -- Illegal!
                    -- This should say ``tagged limited null record''.
            end P1;

7.f         package body P1 is
                type A is access T1'Class;
                Global : A;
                procedure Foo(X : in T1'Class) is
                begin
                    Global := new T1'Class'(X);
                        -- This would be illegal if the full view of
                        -- T1 were limited, like it's supposed to be.
                end A;
            end P1;

7.g         with P1;
            package P2 is
                type T2(D : access Integer) -- Trouble!
                        is new P1.T1 with
                    record
                        My_Task : Some_Task_Type; -- More trouble!
                    end record;
            end P2;

7.h         with P1;
            with P2;
            procedure Main is
                Local : aliased Integer;
                Y : P2.T2(A => Local'Access);
            begin
                P1.Foo(Y);
            end Main;

        7.i   If the above example were legal, we would have succeeded in
        making an access value that points to Main.Local after Main has been
        left, and we would also have succeeded in doing an assignment of a
        task object, both of which are supposed to be no-no's.

        7.j   This rule is not needed for private extensions, because they
        inherit their limitedness from their ancestor, and there is a
        separate rule forbidding limited components of the corresponding
        record extension if the parent is nonlimited.

        7.k   Ramification:  A type derived from an untagged private type is
        untagged, even if the full view of the parent is tagged, and even at
        places that can see the parent:

7.l         package P is
                type Parent is private;
            private
                type Parent is tagged
                    record
                        X: Integer;
                    end record;
            end P;

7.m         package Q is
                type T is new Parent;
            end Q;

7.n         with Q; use Q;
            package body P is
                ... T'Class ... -- Illegal!
                Object: T;
                ... Object.X ... -- Illegal!
                ... Parent(Object).X ... -- OK.
            end P;

        7.o   The declaration of T declares an untagged view.  This view is
        always untagged, so T'Class is illegal, it would be illegal to extend
        T, and so forth.  The component name X is never visible for this
        view, although the component is still there -- one can get one's
        hands on it via a type_conversion.  {94-4941.a} {94-4946.a}
        {94-5001.g}

8   {ancestor subtype (of a private_extension_declaration)} The ancestor
subtype of a private_extension_declaration is the subtype defined by the
ancestor_subtype_indication; the ancestor type shall be a specific tagged
type.  The full view of a private extension shall be derived (directly or
indirectly) from the ancestor type.  In addition to the places where Legality
Rules normally apply (see 12.3), the requirement that the ancestor be
specific applies also in the private part of an instance of a generic unit.

        8.a   Reason:  This rule allows the full view to be defined through
        several intermediate derivations, possibly from a series of types
        produced by generic_instantiations.

9   If the declaration of a partial view includes a known_discriminant_part,
then the full_type_declaration shall have a fully conforming [(explicit)]
known_discriminant_part [(see 6.3.1, ``Conformance Rules'')].  {full
conformance (required)} [The ancestor subtype may be unconstrained; the
parent subtype of the full view is required to be constrained (see 3.7).]

        9.a   Discussion:  If the ancestor subtype has discriminants, then it
        is usually best to make it unconstrained.

        9.b   Ramification:  If the partial view has a known_discriminant_
        part, then the full view has to be a composite, non-array type, since
        only such types may have known discriminants.  {94-4493.c} Also, the
        full view cannot inherit the discriminants in this case; the known_
        discriminant_part has to be explicit.

        9.c   That is, the following is illegal:

9.d         package P is
                type T(D : Integer) is private;
            private
                type T is new Some_Other_Type; -- Illegal!
            end P;

        9.e   even if Some_Other_Type has an integer discriminant called D.

        9.f   It is a ramification of this and other rules that in order for
        a tagged type to privately inherit unconstrained discriminants, the
        private type declaration has to have an unknown_discriminant_part.

10   If a private extension inherits known discriminants from the ancestor
subtype, then the full view shall also inherit its discriminants from the
ancestor subtype, and the parent subtype of the full view shall be
constrained if and only if the ancestor subtype is constrained.

        10.a   Reason:  The first part ensures that the full view has the
        same discriminants as the partial view.  The second part ensures that
        if the partial view is unconstrained, then the full view is also
        unconstrained; otherwise, a client might constrain the partial view
        in a way that conflicts with the constraint on the full view.

11   [If a partial view has unknown discriminants, then the full_type_
declaration may define a definite or an indefinite subtype, with or without
discriminants.]  {94-4474.a} {94-4886.a}

12   If a partial view has neither known nor unknown discriminants, then the
full_type_declaration shall define a definite subtype.  {94-4886.a}
{94-4947.a}

13   If the ancestor subtype of a private extension has constrained
discriminants, then the parent subtype of the full view shall impose a
statically matching constraint on those discriminants.  {statically matching
[required]}

        13.a   Ramification:  If the parent type of the full view is not the
        ancestor type, but is rather some descendant thereof, the constraint
        on the discriminants of the parent type might come from the
        declaration of some intermediate type in the derivation chain between
        the ancestor type and the parent type.

        13.b   Reason:  This prevents the following:

13.c        package P is
                type T2 is new T1(Discrim => 3) with private;
            private
                type T2 is new T1(Discrim => 999) -- Illegal!
                    with record ...;
            end P;

        13.d   The constraints in this example do not statically match.

        13.e   If the constraint on the parent subtype of the full view
        depends on discriminants of the full view, then the ancestor subtype
        has to be unconstrained:

13.f        type One_Discrim(A: Integer) is tagged ...;
            ...
            package P is
                type Two_Discrims(B: Boolean; C: Integer) is new One_Discrim wi\
th private;
            private
                type Two_Discrims(B: Boolean; C: Integer) is new One_Discrim(A \
=> C) with
                    record
                        ...
                    end record;
            end P;

        13.g   The above example would be illegal if the private extension
        said ``is new One_Discrim(A => C);'', because then the constraints
        would not statically match.  (Constraints that depend on
        discriminants are not static.)


                              Static Semantics

14   {private type [partial]} A private_type_declaration declares a private
type and its first subtype.  {private extension [partial]} Similarly, a
private_extension_declaration declares a private extension and its first
subtype.

        14.a   Discussion:  {package-private type} A package-private type is
        one declared by a private_type_declaration; that is, a private type
        other than a generic formal private type.  {package-private
        extension} Similarly, a package-private extension is one declared by
        a private_extension_declaration.  These terms are not used in the
        RM9X version of this document.

15   A declaration of a partial view and the corresponding full_type_
declaration define two views of a single type.  The declaration of a partial
view together with the visible part define the operations that are available
to outside program units; the declaration of the full view together with the
private part define other operations whose direct use is possible only within
the declarative region of the package itself.  {characteristics} Moreover,
within the scope of the declaration of the full view, the characteristics of
the type are determined by the full view; in particular, within its scope,
the full view determines the classes that include the type, which components,
entries, and protected subprograms are visible, what attributes and other
predefined operations are allowed, and whether the first subtype is static.
See 7.3.1.

16   A private extension inherits components (including discriminants unless
there is a new discriminant_part specified) and user-defined primitive
subprograms from its ancestor type, in the same way that a record extension
inherits components and user-defined primitive subprograms from its parent
type (see 3.4).

        16.a   To be honest:  If an operation of the parent type is abstract,
        then the abstractness of the inherited operation is different for
        nonabstract record extensions than for nonabstract private extensions
        (see 3.9.3).


                              Dynamic Semantics

17   {elaboration [private_type_declaration]} The elaboration of a private_
type_declaration creates a partial view of a type.  {elaboration [private_
extension_declaration]} The elaboration of a private_extension_declaration
elaborates the ancestor_subtype_indication, and creates a partial view of a
type.


     NOTES
18   (5) The partial view of a type as declared by a private_type_declaration
     is defined to be a composite view (in 3.2).  The full view of the type
     might or might not be composite.  A private extension is also composite,
     as is its full view.

19   (6) Declaring a private type with an unknown_discriminant_part is a way
     of preventing clients from creating uninitialized objects of the type;
     they are then forced to initialize each object by calling some operation
     declared in the visible part of the package.  If such a type is also
     limited, then no objects of the type can be declared outside the scope
     of the full_type_declaration, restricting all object creation to the
     package defining the type.  This allows complete control over all
     storage allocation for the type.  Objects of such a type can still be
     passed as parameters, however.

   19.a   Discussion:  {generic contract/private type contract analogy}
        Packages with private types are analogous to generic packages with
        formal private types, as follows:  The declaration of a
        package-private type is like the declaration of a formal private
        type.  The visible part of the package is like the generic formal
        part; these both specify a contract (that is, a set of operations and
        other things available for the private type).  The private part of
        the package is like an instantiation of the generic; they both give a
        full_type_declaration that specifies implementation details of the
        private type.  The clients of the package are like the body of the
        generic; usage of the private type in these places is restricted to
        the operations defined by the contract.

   19.b   In other words, being inside the package is like being outside the
        generic, and being outside the package is like being inside the
        generic; a generic is like an ``inside-out'' package.

   19.c   This analogy also works for private extensions in the same
        inside-out way.

   19.d   Many of the legality rules are defined with this analogy in mind.
        See, for example, the rules relating to operations of [formal]
        derived types.

   19.e   The completion rules for a private type are intentionally quite
        similar to the matching rules for a generic formal private type.

   19.f   This analogy breaks down in one respect:  a generic actual subtype
        is a subtype, whereas the full view for a private type is always a
        new type.  (We considered allowing the completion of a private_type_
        declaration to be a subtype_declaration, but the semantics just won't
        work.)  This difference is behind the fact that a generic actual type
        can be class-wide, whereas the completion of a private type always
        declares a specific type.

20   (7) The ancestor type specified in a private_extension_declaration and
     the parent type specified in the corresponding declaration of a record
     extension given in the private part need not be the same -- the parent
     type of the full view can be any descendant of the ancestor type.  In
     this case, for a primitive subprogram that is inherited from the
     ancestor type and not overridden, the formal parameter names and default
     expressions (if any) come from the corresponding primitive subprogram of
     the specified ancestor type, while the body comes from the corresponding
     primitive subprogram of the parent type of the full view.  See 3.9.2.


                                  Examples

21   Examples of private type declarations:

22  type Key is private;
    type File_Name is limited private;

23   Example of a private extension declaration:

24  type List is new Ada.Finalization.Controlled with private;


                            Extensions to Ada 83

        24.a   {extensions to Ada 83} The syntax for a private_type_
        declaration is augmented to allow the reserved word tagged.

        24.b   In Ada 83, a private type without discriminants cannot be
        completed with a type with discriminants.  Ada 9X allows the full
        view to have discriminants, so long as they have defaults (that is,
        so long as the first subtype is definite).  This change is made for
        uniformity with generics, and because the rule as stated is simpler
        and easier to remember than the Ada 83 rule.  In the original version
        of Ada 83, the same restriction applied to generic formal private
        types.  However, the restriction was removed by the ARG for generics.
        In order to maintain the ``generic contract/private type contract
        analogy'' discussed above, we have to apply the same rule to
        package-private types.  Note that a private untagged type without
        discriminants can be completed with a tagged type with discriminants
        only if the full view is constrained, because discriminants of tagged
        types cannot have defaults.

                         Wording Changes From Ada 83

        24.c   RM83-7.4.1(4), ``Within the specification of the package that
        declares a private type and before the end of the corresponding full
        type declaration, a restriction applies....'', is subsumed (and
        corrected) by the rule that a type shall be completely defined before
        it is frozen, and the rule that the parent type of a derived type
        declaration shall be completely defined, unless the derived type is a
        private extension.
7.3.1 Private Operations

1   [For a type declared in the visible part of a package or generic package,
certain operations on the type do not become visible until later in the
package -- either in the private part or the body.  {private operations} Such
private operations are available only inside the declarative region of the
package or generic package.]


                              Static Semantics

2   The predefined operators that exist for a given type are determined by
the classes to which the type belongs.  For example, an integer type has a
predefined "+" operator.  In most cases, the predefined operators of a type
are declared immediately after the definition of the type; the exceptions are
explained below.  Inherited subprograms are also implicitly declared
immediately after the definition of the type, except as stated below.

3   For a composite type, the characteristics (see 7.3) of the type are
determined in part by the characteristics of its component types.  At the
place where the composite type is declared, the only characteristics of
component types used are those characteristics visible at that place.  If
later within the immediate scope of the composite type additional
characteristics become visible for a component type, then any corresponding
characteristics become visible for the composite type.  Any additional
predefined operators are implicitly declared at that place.

4   The corresponding rule applies to a type defined by a derived_type_
definition, if there is a place within its immediate scope where additional
characteristics of its parent type become visible.

5   {become nonlimited} {nonlimited type (becoming nonlimited)} {limited type
(becoming nonlimited)} [For example, an array type whose component type is
limited private becomes nonlimited if the full view of the component type is
nonlimited and visible at some later place within the immediate scope of the
array type.  In such a case, the predefined "=" operator is implicitly
declared at that place, and assignment is allowed after that place.]

6   Inherited primitive subprograms follow a different rule.  For a derived_
type_definition, each inherited primitive subprogram is implicitly declared
at the earliest place, if any, within the immediate scope of the type_
declaration, but after the type_declaration, where the corresponding
declaration from the parent is visible.  If there is no such place, then the
inherited subprogram is not declared at all.  [An inherited subprogram that
is not declared at all cannot be named in a call and cannot be overridden,
but for a tagged type, it is possible to dispatch to it.]  {94-4678.a}
{94-4683.a}

7   For a private_extension_declaration, each inherited subprogram is
declared immediately after the private_extension_declaration if the
corresponding declaration from the ancestor is visible at that place.
Otherwise, the inherited subprogram is not declared for the private
extension, [though it might be for the full type].

        7.a   Reason:  There is no need for the ``earliest place within the
        immediate scope'' business here, because a private_extension_
        declaration will be completed with a full_type_declaration, so we can
        hang the necessary private implicit declarations on the full_type_
        declaration.

        7.b   Discussion:  The above rules matter only when the component
        type (or parent type) is declared in the visible part of a package,
        and the composite type (or derived type) is declared within the
        declarative region of that package (possibly in a nested package or a
        child package).

        7.c   Consider:

7.d         package Parent is
                type Root is tagged null record;
                procedure Op1(X : Root);

7.e             type My_Int is range 1..10;
            private
                procedure Op2(X : Root);

7.f             type Another_Int is new My_Int;
                procedure Int_Op(X : My_Int);
            end Parent;

7.g         with Parent; use Parent;
            package Unrelated is
                type T2 is new Root with null record;
                procedure Op2(X : T2);
            end Unrelated;

7.h         package Parent.Child is
                type T3 is new Root with null record;
                -- Op1(T3) implicitly declared here.

7.i             package Nested is
                    type T4 is new Root with null record;
                private
                    ...
                end Nested;
            private
                -- Op2(T3) implicitly declared here.
                ...
            end Parent.Child;

7.j         with Unrelated; use Unrelated;
            package body Parent.Child is
                package body Nested is
                    -- Op2(T4) implicitly declared here.
                end Nested;

7.k             type T5 is new T2 with null record;
            end Parent.Child;

        7.l   Another_Int does not inherit Int_Op, because Int_Op does not
        ``exist'' at the place where Another_Int is declared.

        7.m   Type T2 inherits Op1 and Op2 from Root.  However, the inherited
        Op2 is never declared, because Parent.Op2 is never visible within the
        immediate scope of T2.  T2 explicitly declares its own Op2, but this
        is unrelated to the inherited one -- it does not override the
        inherited one, and occupies a different slot in the type descriptor.

        7.n   T3 inherits both Op1 and Op2.  Op1 is implicitly declared
        immediately after the type declaration, whereas Op2 is declared at
        the beginning of the private part.  Note that if Child were a private
        child of Parent, then Op1 and Op2 would both be implicitly declared
        immediately after the type declaration.

        7.o   T4 is similar to T3, except that the earliest place within T4's
        immediate scope where Root's Op2 is visible is in the body of Nested.

        7.p   If T3 or T4 were to declare a type-conformant Op2, this would
        override the one inherited from Root.  This is different from the
        situation with T2.

        7.q   T5 inherits Op1 and two Op2's from T2.  Op1 is implicitly
        declared immediately after the declaration of T5, as is the Op2 that
        came from Unrelated.Op2.  However, the Op2 that originally came from
        Parent.Op2 is never implicitly declared for T5, since T2's version of
        that Op2 is never visible (anywhere -- it never got declared either).
        {94-4677.a} {94-4682.a} {94-4439.a}

        7.r   For all of these rules, implicit private parts and bodies are
        assumed as needed.

        7.s   It is possible for characteristics of a type to be revealed in
        more than one place:

7.t         package P is
                type Comp1 is private;
            private
                type Comp1 is new Boolean;
            end P;

7.u         package P.Q is
                package R is
                    type Comp2 is limited private;
                    type A is array(Integer range <>) of Comp2;
                private
                    type Comp2 is new Comp1;
                    -- A becomes nonlimited here.
                    -- "="(A, A) return Boolean is implicitly declared here.
                    ...
                end R;
            private
                -- Now we find out what Comp1 really is, which reveals
                -- more information about Comp2, but we're not within
                -- the immediate scope of Comp2, so we don't do anything
                -- about it yet.
            end P.Q;

7.v         package body P.Q is
                package body R is
                    -- Things like "xor"(A,A) return A are implicitly
                    -- declared here.
                end R;
            end P.Q;

        {94-4444.a}

8   [The Class attribute is defined for tagged subtypes in 3.9.  In
addition,] for every subtype S of an untagged private type whose full view is
tagged, the following attribute is defined:

9   S'Class
                Denotes the class-wide subtype corresponding to the full view
                of S. This attribute is allowed only from the beginning of
                the private part in which the full view is declared, until
                the declaration of the full view.  [After the full view, the
                Class attribute of the full view can be used.]


     NOTES
10   (8) Because a partial view and a full view are two different views of
     one and the same type, outside of the defining package the
     characteristics of the type are those defined by the visible part.
     Within these outside program units the type is just a private type or
     private extension, and any language rule that applies only to another
     class of types does not apply.  The fact that the full declaration might
     implement a private type with a type of a particular class (for example,
     as an array type) is relevant only within the declarative region of the
     package itself including any child units.

     11   The consequences of this actual implementation are, however, valid
     everywhere.  For example: any default initialization of components takes
     place; the attribute Size provides the size of the full view;
     finalization is still done for controlled components of the full view;
     task dependence rules still apply to components that are task objects.

12   (9) Partial views provide assignment (unless the view is limited),
     membership tests, selected components for the selection of discriminants
     and inherited components, qualification, and explicit conversion.

13   (10) For a subtype S of a partial view, S'Size is defined (see 13.3).
     For an object A of a partial view, the attributes A'Size and A'Address
     are defined (see 13.3).  The Position, First_Bit, and Last_Bit
     attributes are also defined for discriminants and inherited components.


                                  Examples

14   Example of a type with private operations:

15  package Key_Manager is
       type Key is private;
       Null_Key : constant Key; -- a deferred constant declaration (see 7.4)
       procedure Get_Key(K : out Key);
       function "<" (X, Y : Key) return Boolean;
    private
       type Key is new Natural;
       Null_Key : constant Key := Key'First;
    end Key_Manager;

16  package body Key_Manager is
       Last_Key : Key := Null_Key;
       procedure Get_Key(K : out Key) is
       begin
          Last_Key := Last_Key + 1;
          K := Last_Key;
       end Get_Key;

17     function "<" (X, Y : Key) return Boolean is
       begin
          return Natural(X) < Natural(Y);
       end "<";
    end Key_Manager;


     NOTES
18   (11) Notes on the example:  Outside of the package Key_Manager, the
     operations available for objects of type Key include assignment, the
     comparison for equality or inequality, the procedure Get_Key and the
     operator "<"; they do not include other relational operators such as
     ">=", or arithmetic operators.

     19   The explicitly declared operator "<" hides the predefined operator
     "<" implicitly declared by the full_type_declaration.  Within the body
     of the function, an explicit conversion of X and Y to the subtype
     Natural is necessary to invoke the "<" operator of the parent type.
     Alternatively, the result of the function could be written as not (X >=
     Y), since the operator ">=" is not redefined.

     20   The value of the variable Last_Key, declared in the package body,
     remains unchanged between calls of the procedure Get_Key.  (See also the
     NOTES of 7.2.)


                         Wording Changes From Ada 83

        20.a   The phrase in RM83-7.4.2(7), ``...after the full type
        declaration'', doesn't work in the presence of child units, so we
        define that rule in terms of visibility.

        20.b   The definition of the Constrained attribute for private types
        has been moved to ``Obsolescent Features.''  (The Constrained
        attribute of an object has not been moved there.)



7.4 Deferred Constants

1   [Deferred constant declarations may be used to declare constants in the
visible part of a package, but with the value of the constant given in the
private part.  They may also be used to declare constants imported from other
languages (see Annex B).]


                               Legality Rules

2   [{deferred constant declaration} A deferred constant declaration is an
object_declaration with the reserved word constant but no initialization
expression.]

        2.a   Proof:  This is stated officially in Section 3.

{deferred constant} The constant declared by a deferred constant declaration
is called a deferred constant.  {requires a completion [deferred constant
declaration]} A deferred constant declaration requires a completion, which
shall be a full constant declaration (called the full declaration of the
deferred constant), or a pragma Import (see Annex B).  {full declaration}

3   A deferred constant declaration that is completed by a full constant
declaration shall occur immediately within the visible part of a package_
specification.  For this case, the following additional rules apply to the
corresponding full declaration:

    4  The full declaration shall occur immediately within the private
       part of the same package;

    5  The deferred and full constants shall have the same type;

 5.a    Ramification:  This implies that both the deferred declaration
        and the full declaration have to have a subtype_indication
        rather than an array_type_definition, because each array_type_
        definition would define a new type.

    6  If the subtype defined by the subtype_indication in the deferred
       declaration is constrained, then the subtype defined by the
       subtype_indication in the full declaration shall match it
       statically.  [On the other hand, if the subtype of the deferred
       constant is unconstrained, then the full declaration is still
       allowed to impose a constraint.  The constant itself will be
       constrained, like all constants;]

    7  If the deferred constant declaration includes the reserved word
       aliased, then the full declaration shall also.

 7.a    Ramification:  On the other hand, the full constant can be
        aliased even if the deferred constant is not.

8   [A deferred constant declaration that is completed by a pragma Import
need not appear in the visible part of a package_specification, and has no
full constant declaration.]

9   The completion of a deferred constant declaration shall occur before the
constant is frozen (see 7.4).

        9.a   Change:  Rule moved here from 13.14, ``Freezing Rules'', as per
        WG9 resolution.


                              Dynamic Semantics

10   {elaboration [deferred constant declaration]} The elaboration of a
deferred constant declaration elaborates the subtype_indication or (only
allowed in the case of an imported constant) the array_type_definition.


     NOTES
11   (12) The full constant declaration for a deferred constant that is of a
     given private type or private extension is not allowed before the
     corresponding full_type_declaration.  This is a consequence of the
     freezing rules for types (see 13.14).

   11.a   Ramification:  Multiple or single declarations are allowed for the
        deferred and the full declarations, provided that the equivalent
        single declarations would be allowed.

   11.b   Deferred constant declarations are useful for declaring constants
        of private views, and types with components of private views.  They
        are also useful for declaring access-to-constant objects that
        designate variables declared in the private part of a package.


                                  Examples

12   Examples of deferred constant declarations:

13  Null_Key : constant Key;      -- see 7.3.1

14  CPU_Identifier : constant String(1..8);
    pragma Import(Assembler, CPU_Identifier, Link_Name => "CPU_ID");
                                  -- see B.1


                            Extensions to Ada 83

        14.a   {extensions to Ada 83} In Ada 83, a deferred constant is
        required to be of a private type declared in the same visible part.
        This restriction is removed for Ada 9X; deferred constants can be of
        any type.

        14.b   In Ada 83, a deferred constant declaration was not permitted
        to include a constraint, nor the reserved word aliased.

        14.c   In Ada 83, the rules required conformance of type marks; here
        we require static matching of subtypes if the deferred constant is
        constrained.

        14.d   A deferred constant declaration can be completed with a pragma
        Import.  Such a deferred constant declaration need not be within a
        package_specification.

        14.e   The rules for too-early uses of deferred constants are
        modified in Ada 9X to allow more cases, and catch all errors at
        compile time.  This change is necessary in order to allow deferred
        constants of a tagged type without violating the principle that for a
        dispatching call, there is always an implementation to dispatch to.
        It has the beneficial side-effect of catching some Ada-83-erroneous
        programs at compile time.  The new rule fits in well with the new
        freezing-point rules.  Furthermore, we are trying to convert
        undefined-value problems into bounded errors, and we were having
        trouble for the case of deferred constants.  Furthermore,
        uninitialized deferred constants cause trouble for the shared
        variable / tasking rules, since they are really variable, even though
        they purport to be constant.  In Ada 9X, they cannot be touched until
        they become constant.

        14.f   Note that we do not consider this change to be an upward
        incompatibility, because it merely changes an erroneous execution in
        Ada 83 into a compile-time error.

        14.g   The Ada 83 semantics are unclear in the case where the full
        view turns out to be an access type.  It is a goal of the language
        design to prevent uninitialized access objects.  One wonders if the
        implementation is required to initialize the deferred constant to
        null, and then initialize it (again!) to its real value.  In Ada 9X,
        the problem goes away.

                         Wording Changes From Ada 83

        14.h   Since deferred constants can now be of a nonprivate type, we
        have made this a stand-alone clause, rather than a subclause of 7.3,
        ``Private Types and Private Extensions''.

        14.i   Deferred constant declarations used to have their own syntax,
        but now they are simply a special case of object_declarations.



7.5 Limited Types

1   [{Limited type} [glossary entry]A limited type is (a view of) a type for
which the assignment operation is not allowed.  A nonlimited type is a (view
of a) type for which the assignment operation is allowed.]

        1.a   Discussion:  The concept of the value of a limited type is
        difficult to define, since the abstract value of a limited type often
        extends beyond its physical representation.  In some sense, values of
        a limited type cannot be divorced from their object.  The value is
        the object.

        1.b   In Ada 83, in the two places where limited types were defined
        by the language, namely tasks and files, an implicit level of
        indirection was implied by the semantics to avoid the separation of
        the value from an associated object.  In Ada 9X, most limited types
        are passed by reference, and even return-ed by reference.

        1.c   To be honest:  For a limited partial view whose full view is
        nonlimited, assignment is possible on parameter passing and function
        return.  To prevent any copying whatsoever, one should make both the
        partial and full views limited.


                               Legality Rules

2   If a tagged record type has any limited components, then the reserved
word limited shall appear in its record_type_definition.

        2.a   Reason:  This prevents tagged limited types from becoming
        nonlimited.  Otherwise, the following could happen:

2.b         package P is
                type T is limited private;
                type R is tagged
                    record -- Illegal!
                           -- This should say ``limited record''.
                        X : T;
                    end record;
            private
                type T is new Integer; -- R becomes nonlimited here.
            end P;

2.c         package Q is
                type R2(Access_Discrim : access ...) is new R with
                    record
                        Y : Some_Task_Type;
                    end record;
            end Q;

        2.d   If the above were legal, then assignment would be defined for
        R'Class in the body of P, which is bad news, given the access
        discriminant and the task.


                              Static Semantics

3   {limited type} A type is limited if it is a descendant of one of the
following:

    4  a type with the reserved word limited in its definition;

 4.a    Ramification:  Note that there is always a ``definition,''
        conceptually, even if there is no syntactic category called
        ``..._definition''.

    5  a task or protected type;

    6  a composite type with a limited component.

7   {nonlimited type} Otherwise, the type is nonlimited.

8   [There are no predefined equality operators for a limited type.]


     NOTES
9    (13) The following are consequences of the rules for limited types:

        10  An initialization expression is not allowed in an object_
            declaration if the type of the object is limited.

        11  A default expression is not allowed in a component_
            declaration if the type of the record component is limited.

        12  An initialized allocator is not allowed if the designated
            type is limited.

        13  A generic formal parameter of mode in must not be of a
            limited type.

14   (14) Aggregates are not available for a limited composite type.
     Concatenation is not available for a limited array type.

15   (15) The rules do not exclude a default_expression for a formal
     parameter of a limited type; they do not exclude a deferred constant of
     a limited type if the full declaration of the constant is of a
     nonlimited type.

16   (16) {become nonlimited} {nonlimited type (becoming nonlimited)}
     {limited type (becoming nonlimited)} As illustrated in 7.3.1, an
     untagged limited type can become nonlimited under certain circumstances.

   16.a   Ramification:  Limited private types do not become nonlimited;
        instead, their full view can be nonlimited, which has a similar
        effect.

   16.b   It is important to remember that a single nonprivate type can be
        both limited and nonlimited in different parts of its scope.  In
        other words, ``limited'' is a property that depends on where you are
        in the scope of the type.  We don't call this a ``view property''
        because there is no particular declaration to declare the nonlimited
        view.

   16.c   Tagged types never become nonlimited.


                                  Examples

17   Example of a package with a limited type:

18  package IO_Package is
       type File_Name is limited private;

19     procedure Open (F : in out File_Name);
       procedure Close(F : in out File_Name);
       procedure Read (F : in File_Name; Item : out Integer);
       procedure Write(F : in File_Name; Item : in  Integer);
    private
       type File_Name is
          limited record
             Internal_Name : Integer := 0;
          end record;
    end IO_Package;

20  package body IO_Package is
       Limit : constant := 200;
       type File_Descriptor is record  ...  end record;
       Directory : array (1 .. Limit) of File_Descriptor;
       ...
       procedure Open (F : in out File_Name) is  ...  end;
       procedure Close(F : in out File_Name) is  ...  end;
       procedure Read (F : in File_Name; Item : out Integer) is ... end;
       procedure Write(F : in File_Name; Item : in  Integer) is ... end;
    begin
       ...
    end IO_Package;


     NOTES
21   (17) Notes on the example:  In the example above, an outside subprogram
     making use of IO_Package may obtain a file name by calling Open and
     later use it in calls to Read and Write.  Thus, outside the package, a
     file name obtained from Open acts as a kind of password; its internal
     properties (such as containing a numeric value) are not known and no
     other operations (such as addition or comparison of internal names) can
     be performed on a file name.  Most importantly, clients of the package
     cannot make copies of objects of type File_Name.

     22   This example is characteristic of any case where complete control
     over the operations of a type is desired.  Such packages serve a dual
     purpose.  They prevent a user from making use of the internal structure
     of the type.  They also implement the notion of an encapsulated data
     type where the only operations on the type are those given in the
     package specification.

     23   The fact that the full view of File_Name is explicitly declared
     limited means that parameter passing and function return will always be
     by reference (see 6.2 and 6.5).
                            Extensions to Ada 83

        23.a   {extensions to Ada 83} The restrictions in RM83-7.4.4(4),
        which disallowed out parameters of limited types in certain cases,
        are removed.

                         Wording Changes From Ada 83

        23.b   Since limitedness and privateness are orthogonal in Ada 9X
        (and to some extent in Ada 83), this is now its own clause rather
        than being a subclause of 7.3, ``Private Types and Private
        Extensions''.



7.6 User-Defined Assignment and Finalization

1   [{user-defined assignment} {assignment (user-defined)} Three kinds of
actions are fundamental to the manipulation of objects:  initialization,
finalization, and assignment.  Every object is initialized, either explicitly
or by default, after being created (for example, by an object_declaration or
allocator).  Every object is finalized before being destroyed (for example,
by leaving a subprogram_body containing an object_declaration, or by a call
to an instance of Unchecked_Deallocation).  An assignment operation is used
as part of assignment_statements, explicit initialization, parameter passing,
and other operations.  {constructor: see initialization} {constructor: see
Initialize} {destructor: see finalization}

2   Default definitions for these three fundamental operations are provided
by the language, but {controlled type} a controlled type gives the user
additional control over parts of these operations.

        2.a   Glossary entry:  {Controlled type} A controlled type supports
        user-defined assignment and finalization.  Objects are always
        finalized before being destroyed.

{Initialize} {Finalize} {Adjust} In particular, the user can define, for a
controlled type, an Initialize procedure which is invoked immediately after
the normal default initialization of a controlled object, a Finalize
procedure which is invoked immediately before finalization of any of the
components of a controlled object, and an Adjust procedure which is invoked
as the last step of an assignment to a (nonlimited) controlled object.]

        2.b   Ramification:  Here's the basic idea of initialization, value
        adjustment, and finalization, whether or not user defined:  When an
        object is created, if it is explicitly assigned an initial value, the
        assignment copies and adjusts the initial value.  Otherwise,
        Initialize is applied to it (except in the case of an aggregate as a
        whole).  An assignment_statement finalizes the target before copying
        in and adjusting the new value.  Whenever an object goes away, it is
        finalized.  Calls on Initialize and Adjust happen bottom-up; that is,
        components first, followed by the containing object.  Calls on
        Finalize happens top-down; that is, first the containing object, and
        then its components.  These ordering rules ensure that any components
        will be in a well-defined state when Initialize, Adjust, or Finalize
        is applied to the containing object.


                              Static Semantics

3   The following language-defined library package exists:

4
    package Ada.Finalization is
        pragma Preelaborate(Finalization);{94-4528.a}

5       type Controlled is abstract tagged private;

6       procedure Initialize(Object : in out Controlled);
        procedure Adjust                 (Object : in out Controlled);
        procedure Finalize               (Object : in out Controlled);

7       type Limited_Controlled is abstract tagged limited private;

8
        procedure Initialize(Object : in out Limited_Controlled);
        procedure Finalize  (Object : in out Limited_Controlled);
    private
        ... -- not specified by the language
    end Ada.Finalization;

9   {controlled type} A controlled type is a descendant of Controlled or
Limited_Controlled.

        9.a   Discussion:  We say ``nonlimited controlled types'' when we
        want to talk about descendants of Controlled only.

The (default) implementations of Initialize, Adjust, and Finalize have no
effect.  The predefined "=" operator of type Controlled always returns True,
[since this operator is incorporated into the implementation of the
predefined equality operator of types derived from Controlled, as explained
in 4.5.2.]  {94-4619.a} {94-4843.a} The type Limited_Controlled is like
Controlled, except that it is limited and it lacks the primitive subprogram
Adjust.

        9.b   Reason:  We considered making Adjust and Finalize abstract.
        However, a reasonable coding convention is e.g. for Finalize to
        always call the parent's Finalize after doing whatever work is needed
        for the extension part.  (Unlike CLOS, we have no way to do that
        automatically in Ada 9X.)  For this to work, Finalize cannot be
        abstract.  In a generic unit, for a generic formal abstract derived
        type whose ancestor is Controlled or Limited_Controlled, calling the
        ancestor's Finalize would be illegal if it were abstract, even though
        the actual type might have a concrete version.

        9.c   Types Controlled and Limited_Controlled are abstract, even
        though they have no abstract primitive subprograms.  It is not clear
        that they need to be abstract, but there seems to be no harm in it,
        and it might make an implementation's life easier to know that there
        are no objects of these types -- in case the implementation wishes to
        make them ``magic'' in some way.


                              Dynamic Semantics

10   {elaboration [object_declaration]} During the elaboration of an object_
declaration, for every controlled subcomponent of the object that is not
assigned an initial value (as defined in 3.3.1), Initialize is called on that
subcomponent.  Similarly, if the object as a whole is controlled and is not
assigned an initial value, Initialize is called on the object.  The same
applies to the evaluation of an allocator, as explained in 4.8.

11   For an extension_aggregate whose ancestor_part is a subtype_mark,
Initialize is called on all controlled subcomponents of the ancestor part; if
the type of the ancestor part is itself controlled, the Initialize procedure
of the ancestor type is called, unless that Initialize procedure is abstract.

        11.a   Discussion:  Example:

11.b        type T1 is new Controlled with
                record
                    ... -- some components might have defaults
                end record;

11.c        type T2 is new Controlled with
                record
                    X : T1; -- no default
                    Y : T1 := ...; -- default
                end record;

11.d        A : T2;
            B : T2 := ...;

        11.e   As part of the elaboration of A's declaration, A.Y is assigned
        a value; therefore Initialize is not applied to A.Y.  Instead, Adjust
        is applied to A.Y as part of the assignment operation.  Initialize is
        applied to A.X and to A, since those objects are not assigned an
        initial value.  The assignment to A.Y is not considered an assignment
        to A.

        11.f   For the elaboration of B's declaration, Initialize is not
        called at all.  Instead the assignment adjusts B's value; that is, it
        applies Adjust to B.X, B.Y, and B.

12   Initialize and other initialization operations are done in an arbitrary
order, except as follows.  Initialize is applied to an object after
initialization of its subcomponents, if any [(including both implicit
initialization and Initialize calls)].  If an object has a component with an
access discriminant constrained by a per-object expression, Initialize is
applied to this component after any components that do not have such
discriminants.  For an object with several components with such a
discriminant, Initialize is applied to them in order of their component_
declarations.  For an allocator, any task activations follow all calls on
Initialize.

        12.a   Reason:  The fact that Initialize is done for subcomponents
        first allows Initialize for a composite object to refer to its
        subcomponents knowing they have been properly initialized.

        12.b   The fact that Initialize is done for components with access
        discriminants after other components allows the Initialize operation
        for a component with a self-referential access discriminant to assume
        that other components of the enclosing object have already been
        properly initialized.  For multiple such components, it allows some
        predictability.

13   {assignment operation} When a target object with any controlled parts is
assigned a value, [either when created or in a subsequent assignment_
statement,] the assignment operation proceeds as follows:

   14  The value of the target becomes the assigned value.

   15  {adjusting the value of an object} {adjustment} The value of the
       target is adjusted.

        15.a   Ramification:  If any parts of the object are controlled,
        abort is deferred during the assignment operation.

16   {adjusting the value of an object} {adjustment} To adjust the value of a
[(nonlimited)] composite object, the values of the components of the object
are first adjusted in an arbitrary order, and then, if the object is
controlled, Adjust is called.  Adjusting the value of an elementary object
has no effect[, nor does adjusting the value of a composite object with no
controlled parts.]

        16.a   Ramification:  Adjustment is never performed for values of a
        by-reference limited type, since these types do not support copying.

        16.b   Reason:  The verbiage in the Initialize rule about access
        discriminants constrained by per-object expressions is not necessary
        here, since such types are limited, and therefore are never adjusted.

17   {execution [assignment_statement]} For an assignment_statement, [ after
the name and expression have been evaluated, and any conversion (including
constraint checking) has been done,] an anonymous object is created, and the
value is assigned into it; [that is, the assignment operation is applied].
[(Assignment includes value adjustment.)]  The target of the assignment_
statement is then finalized.  The value of the anonymous object is then
assigned into the target of the assignment_statement.  Finally, the anonymous
object is finalized.  [As explained below, the implementation may eliminate
the intermediate anonymous object, so this description subsumes the one given
in 5.2, ``Assignment Statements''.]

        17.a   Reason:  An alternative design for user-defined assignment
        might involve an Assign operation instead of Adjust:

17.b        procedure Assign(Target : in out Controlled; Source : in out Contro\
lled);

        17.c   Or perhaps even a syntax like this:

17.d        procedure ":="(Target : in out Controlled; Source : in out Controll\
ed);

        17.e   Assign (or ":=") would have the responsibility of doing the
        copy, as well as whatever else is necessary.  This would have the
        advantage that the Assign operation knows about both the target and
        the source at the same time -- it would be possible to do things like
        reuse storage belonging to the target, for example, which Adjust
        cannot do.  However, this sort of design would not work in the case
        of unconstrained discriminated variables, because there is no way to
        change the discriminants individually.  For example:

17.f        type Mutable(D : Integer := 0) is
                record
                    X : Array_Of_Controlled_Things(1..D);
                    case D is
                        when 17 => Y : Controlled_Thing;
                        when others => null;
                    end D;
                end record;

        17.g   An assignment to an unconstrained variable of type Mutable can
        cause some of the components of X, and the component Y, to appear
        and/or disappear.  There is no way to write the Assign operation to
        handle this sort of case.

        17.h   Forbidding such cases is not an option -- it would cause
        generic contract model violations.


                         Implementation Permissions

18   An implementation is allowed to relax the above rules [(for nonlimited
controlled types)] in the following ways:

        18.a   Proof:  The phrase ``for nonlimited controlled types'' follows
        from the fact that all of the following permissions apply to cases
        involving assignment.  It is important because the programmer can
        count on a stricter semantics for limited controlled types.

   19  For an assignment_statement that assigns to an object the value
       of that same object, the implementation need not do anything.
       {94-4495.a}

 19.a   Ramification:  In other words, even if an object is controlled
        and a combination of Finalize and Adjust on the object might
        have a net side effect, they need not be performed.

   20  For an assignment_statement for a noncontrolled type, the
       implementation may finalize and assign each component of the
       variable separately (rather than finalizing the entire variable
       and assigning the entire new value) unless a discriminant of the
       variable is changed by the assignment.

 20.a   Reason:  For example, in a slice assignment, an anonymous object
        is not necessary if the slice is copied component-by-component
        in the right direction, since array types are not controlled
        (although their components may be).  Note that the direction,
        and even the fact that it's a slice assignment, can in general
        be determined only at run time.

   21  For an aggregate or function call whose value is assigned into a
       target object, the implementation need not create a separate
       anonymous object if it can safely create the value of the
       aggregate or function call directly in the target object.
       Similarly, for an assignment_statement, the implementation need
       not create an anonymous object if the value being assigned is the
       result of evaluating a name denoting an object (the source
       object) whose storage cannot overlap with the target.  If the
       source object might overlap with the target object, then the
       implementation can avoid the need for an intermediary anonymous
       object by exercising one of the above permissions and perform the
       assignment one component at a time (for an overlapping array
       assignment), or not at all (for an assignment where the target
       and the source of the assignment are the same object).  Even if
       an anonymous object is created, the implementation may move its
       value to the target object as part of the assignment without
       re-adjusting so long as the anonymous object has no aliased
       subcomponents.

 21.a   Ramification:  In the aggregate case, only one value adjustment
        is necessary, and there is no anonymous object to be finalized.

 21.b   In the assignment_statement case as well, no finalization of the
        anonymous object is needed.  On the other hand, if the target
        has aliased subcomponents, then an adjustment takes place
        directly on the target object as the last step of the
        assignment, since some of the subcomponents may be
        self-referential or otherwise position-dependent.


                            Extensions to Ada 83

        21.c   {extensions to Ada 83} Controlled types and user-defined
        finalization are new to Ada 9X.  (Ada 83 had finalization semantics
        only for masters of tasks.)



7.6.1 Completion and Finalization

1   [This subclause defines completion and leaving of the execution of
constructs and entities.  A master is the execution of a construct that
includes finalization of local objects after it is complete (and after
waiting for any local tasks -- see 9.3), but before leaving.  {94-4715.a}
Other constructs and entities are left immediately upon completion.
{cleanup: see finalization} {destructor: see finalization}]


                              Dynamic Semantics

2   {completion and leaving (completed and left)} {completion (run-time
concept)} The execution of a construct or entity is complete when the end of
that execution has been reached, or when a transfer of control (see 5.1)
causes it to be abandoned.  {normal completion} {completion (normal)}
{abnormal completion} {completion (abnormal)} Completion due to reaching the
end of execution, or due to the transfer of control of an exit_, return_,
goto_, or requeue_statement or of the selection of a terminate_alternative is
normal completion.  Completion is abnormal otherwise [-- when control is
transferred out of a construct due to abort or the raising of an exception].

        2.a   Discussion:  Don't confuse the run-time concept of completion
        with the compile-time concept of completion defined in 3.11.1.

3   {leaving} {left} After execution of a construct or entity is complete, it
is left, meaning that execution continues with the next action, as defined
for the execution that is taking place.  {master} Leaving an execution
happens immediately after its completion, except in the case of a master:
the execution of a task_body, a block_statement, a subprogram_body, an entry_
body, or an accept_statement.  A master is finalized after it is complete,
and before it is left.  {94-4715.a}

        3.a   Reason:  Note that although an accept_statement has no
        declarative_part, it can call functions and evaluate aggregates,
        possibly causing anonymous controlled objects to be created, and we
        don't want those objects to escape outside the rendezvous.

4   {finalization (of a master)} For the finalization of a master, dependent
tasks are first awaited, as explained in 9.3.  Then each object whose
accessibility level is the same as that of the master is finalized if the
object was successfully initialized and still exists.  {94-4715.a} [These
actions are performed whether the master is left by reaching the last
statement or via a transfer of control.]

        4.a   Ramification:  As explained in 3.10.2, the set of objects with
        the same accessibility level as that of the master includes objects
        declared immediately within the master, objects declared in nested
        packages, objects created by allocators (if the ultimate ancestor
        access type is declared in one of those places) and subcomponents of
        all of these things.  If an object was already finalized by
        Unchecked_Deallocation, then it is not finalized again when the
        master is left.

        4.b   Note that any object whose accessibility level is deeper than
        that of the master would no longer exist; those objects would have
        been finalized by some inner master.  Thus, after leaving a master,
        the only objects yet to be finalized are those whose accessibility
        level is less deep than that of the master.  {94-4715.a}

        4.c   To be honest:  Subcomponents of objects due to be finalized are
        not finalized by the finalization of the master; they are finalized
        by the finalization of the containing object.

        4.d   Reason:  We need to finalize subcomponents of objects even if
        the containing object is not going to get finalized because it was
        not fully initialized.  But if the containing object is finalized, we
        don't want to require repeated finalization of the subcomponents, as
        might normally be implied by the recursion in finalization of a
        master and the recursion in finalization of an object.

When a transfer of control causes completion of an execution, each included
master is finalized in order, from innermost outward.

        4.e   To be honest:  Formally, completion and leaving refer to
        executions of constructs or entities.  However, the standard
        sometimes (informally) refers to the constructs or entities whose
        executions are being completed.  Thus, for example, ``the subprogram_
        call or task is complete'' really means ``the execution of the
        subprogram_call or task is complete.''

5   {finalization (of an object) [distributed]} For the finalization of an
object:

    6  If the object is of an elementary type, finalization has no
       effect;

    7  If the object is of a controlled type, the Finalize procedure is
       called;

    8  If the object is of a protected type, the actions defined in 9.4
       are performed;

    9  If the object is of a composite type, then after performing the
       above actions, if any, every component of the object is finalized
       in an arbitrary order, except as follows:  if the object has a
       component with an access discriminant constrained by a per-object
       expression, this component is finalized before any components
       that do not have such discriminants; for an object with several
       components with such a discriminant, they are finalized in the
       reverse of the order of their component_declarations.

 9.a    Reason:  This allows the finalization of a component with an
        access discriminant to refer to other components of the
        enclosing object prior to their being finalized.

10   {execution [instance of Unchecked_Deallocation]} Immediately before an
instance of Unchecked_Deallocation reclaims the storage of an object, the
object is finalized.  [If an instance of Unchecked_Deallocation is never
applied to an object created by an allocator, the object will still exist
when the corresponding master completes, and it will be finalized then.]

11   The order in which the finalization of a master performs finalization of
objects is as follows:  Objects created by declarations in the master are
finalized in the reverse order of their creation.  For objects that were
created by allocators for an access type whose ultimate ancestor is declared
in the master, this rule is applied as though each such object that still
exists had been created in an arbitrary order at the first freezing point
(see 13.14) of the ultimate ancestor type.

        11.a   Reason:  Note that we talk about the type of the allocator
        here.  There may be access values of a (general) access type pointing
        at objects created by allocators for some other type; these are not
        finalized at this point.

        11.b   The freezing point of the ultimate ancestor access type is
        chosen because before that point, pool elements cannot be created,
        and after that point, access values designating (parts of) the pool
        elements can be created.  This is also the point after which the pool
        object cannot have been declared.  We don't want to finalize the pool
        elements until after anything finalizing objects that contain access
        values designating them.  Nor do we want to finalize pool elements
        after finalizing the pool object itself.

        11.c   Ramification:  Finalization of allocated objects is done
        according to the (ultimate ancestor) allocator type, not according to
        the storage pool in which they are allocated.  Pool finalization
        might reclaim storage (see 13.11, ``Storage Management''), but has
        nothing (directly) to do with finalization of the pool elements.

        11.d   Note that finalization is done only for objects that still
        exist; if an instance of Unchecked_Deallocation has already gotten
        rid of a given pool element, that pool element will not be finalized
        when the master is left.

        11.e   Note that a deferred constant declaration does not create the
        constant; the full constant declaration creates it.  Therefore, the
        order of finalization depends on where the full constant declaration
        occurs, not the deferred constant declaration.

        11.f   An imported object is not created by its declaration.  It is
        neither initialized nor finalized.

        11.g   Implementation Note:  An implementation has to ensure that the
        storage for an object is not reclaimed when references to the object
        are still possible (unless, of course, the user explicitly requests
        reclamation via an instance of Unchecked_Deallocation).  This
        implies, in general, that objects cannot be deallocated one by one as
        they are finalized; a subsequent finalization might reference an
        object that has been finalized, and that object had better be in its
        (well-defined) finalized state.

12   {execution [assignment_statement]} The target of an assignment statement
is finalized before copying in the new value, as explained in 7.6.

13   The anonymous objects created by function calls and by aggregates are
finalized no later than the end of the innermost enclosing declarative_item
or statement; if that is a compound_statement, they are finalized before
starting the execution of any statement within the compound_statement.

        13.a   To be honest:  This is not to be construed as permission to
        call Finalize asynchronously with respect to normal user code.  For
        example,

13.b        declare
                X : Some_Controlled_Type := F(G(...));
                -- The anonymous objects created for F and G are finalized
                -- no later than this point.
                Y : ...
            begin
                ...
            end;

        13.c   The anonymous object for G should not be finalized at some
        random point in the middle of the body of F, because F might
        manipulate the same data structures as the Finalize operation,
        resulting in erroneous access to shared variables.

        13.d   Reason:  It might be quite inconvenient for the implementation
        to defer finalization of the anonymous object for G until after
        copying the value of F into X, especially if the size of the result
        is not known at the call site.


                          Bounded (Run-Time) Errors

14   {bounded error} It is a bounded error for a call on Finalize or Adjust
to propagate an exception.  The possible consequences depend on what action
invoked the Finalize or Adjust operation:

        14.a   Ramification:  It is not a bounded error for Initialize to
        propagate an exception.  If Initialize propagates an exception, then
        no further calls on Initialize are performed, and those components
        that have already been initialized (either explicitly or by default)
        are finalized in the usual way.

   15  {Program_Error (raised by failure of run-time check)} For a
       Finalize invoked as part of an assignment_statement, Program_
       Error is raised at that point.

   16  {Program_Error (raised by failure of run-time check)} For an
       Adjust invoked as part of an assignment operation, any other
       adjustments due to be performed are performed, and then Program_
       Error is raised.

   17  {Program_Error (raised by failure of run-time check)} For a
       Finalize invoked as part of a call on an instance of Unchecked_
       Deallocation, any other finalizations due to be performed are
       performed, and then Program_Error is raised.

   18  {Program_Error (raised by failure of run-time check)} For a
       Finalize invoked by the transfer of control of an exit_, return_,
       goto_, or requeue_statement, Program_Error is raised no earlier
       than after the finalization of the master being finalized when
       the exception occurred, and no later than the point where normal
       execution would have continued.  Any other finalizations due to
       be performed up to that point are performed before raising
       Program_Error.

 18.a   Ramification:  For example, upon leaving a block_statement due
        to a goto_statement, the Program_Error would be raised at the
        point of the target statement denoted by the label, or else in
        some more dynamically nested place, but not so nested as to
        allow an exception_handler that has visibility upon the
        finalized object to handle it.  For example,

18.b        procedure Main is
            begin
                <<The_Label>>
                Outer_Block_Statement : declare
                    X : Some_Controlled_Type;
                begin
                    Inner_Block_Statement : declare
                        Y : Some_Controlled_Type;
                        Z : Some_Controlled_Type;
                    begin
                        goto The_Label;
                    exception
                        when Program_Error => ... -- Handler number 1.
                    end;
                exception
                    when Program_Error => ... -- Handler number 2.
                end;
            exception
                when Program_Error => ... -- Handler number 3.
            end Main;

 18.c   The goto_statement will first cause Finalize(Y) to be called.
        Suppose that Finalize(Y) propagates an exception.  Program_Error
        will be raised after leaving Inner_Block_Statement, but before
        leaving Main.  Thus, handler number 1 cannot handle this
        Program_Error; it will be handled either by handler number 2 or
        handler number 3.  If it is handled by handler number 2, then
        Finalize(Z) will be done before executing the handler.  If it is
        handled by handler number 3, then Finalize(Z) and Finalize(X)
        will both be done before executing the handler.

   19  For a Finalize invoked by a transfer of control that is due to
       raising an exception, any other finalizations due to be performed
       for the same master are performed; Program_Error is raised
       immediately after leaving the master.

 19.a   Ramification:  If, in the above example, the goto_statement were
        replaced by a raise_statement, then the Program_Error would be
        handled by handler number 2, and Finalize(Z) would be done
        before executing the handler.

 19.b   Reason:  We considered treating this case in the same way as the
        others, but that would render certain exception_handlers
        useless.  For example, suppose the only exception_handler is one
        for others in the main subprogram.  If some deeply nested call
        raises an exception, causing some Finalize operation to be
        called, which then raises an exception, then normal execution
        ``would have continued'' at the beginning of the exception_
        handler.  Raising Program_Error at that point would cause that
        handler's code to be skipped.  One would need two nested
        exception_handlers to be sure of catching such cases!

 19.c   On the other hand, the exception_handler for a given master
        should not be allowed to handle exceptions raised during
        finalization of that master.

   20  For a Finalize invoked by a transfer of control due to an abort
       or selection of a terminate alternative, the exception is
       ignored; any other finalizations due to be performed are
       performed.

 20.a   Ramification:  This case includes an asynchronous transfer of
        control.

 20.b   To be honest:  {Program_Error (raised by failure of run-time
        check)} This violates the general principle that it is always
        possible for a bounded error to raise Program_Error (see 1.1.5,
        ``Classification of Errors'').


     NOTES
21   (18) The rules of Section 10 imply that immediately prior to partition
     termination, Finalize operations are applied to library-level controlled
     objects (including those created by allocators of library-level access
     types, except those already finalized).  This occurs after waiting for
     library-level tasks to terminate.

   21.a   Discussion:  We considered defining a pragma that would apply to a
        controlled type that would suppress Finalize operations for
        library-level objects of the type upon partition termination.  This
        would be useful for types whose finalization actions consist of
        simply reclaiming global heap storage, when this is already provided
        automatically by the environment upon program termination.

22   (19) A constant is only constant between its initialization and
     finalization.  Both initialization and finalization are allowed to
     change the value of a constant.

23   (20) Abort is deferred during certain operations related to controlled
     types, as explained in 9.8.  Those rules prevent an abort from causing a
     controlled object to be left in an ill-defined state.

24   (21) The Finalize procedure is called upon finalization of a controlled
     object, even if Finalize was called earlier, either explicitly or as
     part of an assignment; hence, if a controlled type is visibly controlled
     (implying that its Finalize primitive is directly callable), or is
     nonlimited (implying that assignment is allowed), its Finalize procedure
     should be designed to have no ill effect if it is applied a second time
     to the same object.

   24.a   Discussion:  Or equivalently, a Finalize procedure should be
        ``idempotent''; applying it twice to the same object should be
        equivalent to applying it once.

   24.b   Reason:  A user-written Finalize procedure should be idempotent
        since it can be called explicitly by a client (at least if the type
        is "visibly" controlled).  Also, Finalize is used implicitly as part
        of the assignment_statement if the type is nonlimited, and an abort
        is permitted to disrupt an assignment_statement between finalizing
        the left-hand side and assigning the new value to it (an abort is not
        permitted to disrupt an assignment operation between copying in the
        new value and adjusting it).

   24.c   Discussion:  Either Initialize or Adjust, but not both, is applied
        to (almost) every controlled object when it is created:  Initialize
        is done when no initial value is assigned to the object, whereas
        Adjust is done as part of assigning the initial value.  The one
        exception is the anonymous object created by an aggregate; Initialize
        is not applied to the aggregate as a whole, nor is the value of the
        aggregate adjusted.

   24.d   {assignment operation (list of uses)} All of the following use the
        assignment operation, and thus perform value adjustment:

         24.e  the assignment_statement (see 5.2);

         24.f  explicit initialization of a stand-alone object (see
               3.3.1) or of a pool element (see 4.8);

         24.g  default initialization of a component of a stand-alone
               object or pool element (in this case, the value of each
               component is assigned, and therefore adjusted, but the
               value of the object as a whole is not adjusted);

         24.h  function return, when the result type is not a
               return-by-reference type (see 6.5); (adjustment of the
               result happens before finalization of the function;
               values of return-by-reference types are not adjusted);

         24.i  predefined operators (although the only one that matters
               is concatenation; see 4.5.3);

         24.j  generic formal objects of mode in (see 12.4); these are
               defined in terms of constant_declarations; and

         24.k  aggregates (see 4.3) (in this case, the value of each
               component, and the parent part, for an extension_
               aggregate, is assigned, and therefore adjusted, but the
               value of the aggregate as a whole is not adjusted;
               neither is Initialize called);

   24.l   The following also use the assignment operation, but adjustment
        never does anything interesting in these cases:

         24.m  By-copy parameter passing uses the assignment operation
               (see 6.4.1), but controlled objects are always passed by
               reference, so the assignment operation never does
               anything interesting in this case.  If we were to allow
               by-copy parameter passing for controlled objects, we
               would need to make sure that the actual is finalized
               before doing the copy back for [in] out parameters.  The
               finalization of the parameter itself needs to happen
               after the copy back (if any), similar to the finalization
               of an anonymous function return object or aggregate
               object.

         24.n  For loops use the assignment operation (see 5.5), but
               since the type of the loop parameter is never controlled,
               nothing interesting happens there, either.

   24.o   Because Controlled and Limited_Controlled are library-level tagged
        types, all controlled types will be library-level types, because of
        the accessibility rules (see 3.10.2 and 3.9.1).  This ensures that
        the Finalize operations may be applied without providing any
        ``display'' or ``static-link.''  This simplifies finalization as a
        result of garbage collection, abort, and asynchronous transfer of
        control.

   24.p   Finalization of the parts of a protected object are not done as
        protected actions.  It is possible (in pathological cases) to create
        tasks during finalization that access these parts in parallel with
        the finalization itself.  This is an erroneous use of shared
        variables.

   24.q   Implementation Note:  One implementation technique for finalization
        is to chain the controlled objects together on a per-task list.  When
        leaving a master, the list can be walked up to a marked place.  The
        links needed to implement the list can be declared (privately) in
        types Controlled and Limited_Controlled, so they will be inherited by
        all controlled types.

   24.r   Another implementation technique, which we refer to as the
        ``PC-map'' approach essentially implies inserting exception handlers
        at various places, and finalizing objects based on where the
        exception was raised.

   24.s   {PC-map approach to finalization} {program-counter-map approach to
        finalization} The PC-map approach is for the compiler/linker to
        create a map of code addresses; when an exception is raised, or abort
        occurs, the map can be consulted to see where the task was executing,
        and what finalization needs to be performed.  This approach was given
        in the Ada 83 Rationale as a possible implementation strategy for
        exception handling -- the map is consulted to determine which
        exception handler applies.

   24.t   If the PC-map approach is used, the implementation must take care
        in the case of arrays.  The generated code will generally contain a
        loop to initialize an array.  If an exception is raised part way
        through the array, the components that have been initialized must be
        finalized, and the others must not be finalized.

   24.u   It is our intention that both of these implementation methods
        should be possible.


                         Wording Changes From Ada 83

        24.v   Finalization depends on the concepts of completion and
        leaving, and on the concept of a master.  Therefore, we have moved
        the definitions of these concepts here, from where they used to be in
        Section 9.  These concepts also needed to be generalized somewhat.
        Task waiting is closely related to user-defined finalization; the
        rules here refer to the task-waiting rules of Section 9.



                         Section 8: Visibility Rules


1   [The rules defining the scope of declarations and the rules defining
which identifiers, character_literals, and operator_symbols are visible at
(or from) various places in the text of the program are described in this
section.  The formulation of these rules uses the notion of a declarative
region.

2   As explained in Section 3, a declaration declares a view of an entity and
associates a defining name with that view.  The view comprises an
identification of the viewed entity, and possibly additional properties.  A
usage name denotes a declaration.  It also denotes the view declared by that
declaration, and denotes the entity of that view.  Thus, two different usage
names might denote two different views of the same entity; in this case they
denote the same entity.]
        2.a   To be honest:  In some cases, a usage name that denotes a
        declaration does not denote the view declared by that declaration,
        nor the entity of that view, but instead denotes a view of the
        current instance of the entity, and denotes the current instance of
        the entity.  This sometimes happens when the usage name occurs inside
        the declarative region of the declaration.


                         Wording Changes From Ada 83

        2.b   We no longer define the term ``basic operation;'' thus we no
        longer have to worry about the visibility of them.  Since they were
        essentially always visible in Ada 83, this change has no effect.  The
        reason for this change is that the definition in Ada 83 was
        confusing, and not quite correct, and we found it difficult to fix.
        For example, one wonders why an if_statement was not a basic
        operation of type Boolean.  For another example, one wonders what it
        meant for a basic operation to be ``inherent in'' something.
        Finally, this fixes the problem addressed by AI-00027/07.



8.1 Declarative Region

                              Static Semantics

1   {declarative region (of a construct)} For each of the following
constructs, there is a portion of the program text called its declarative
region, [within which nested declarations can occur]:

    2  any declaration, other than that of an enumeration type, that is
       not a completion [of a previous declaration];

    3  a block_statement;

    4  a loop_statement;

    5  an accept_statement;

    6  an exception_handler.

7   The declarative region includes the text of the construct together with
additional text determined [(recursively)], as follows:

    8  If a declaration is included, so is its completion, if any.

    9  If the declaration of a library unit [(including Standard -- see
       10.1.1)] is included, so are the declarations of any child units
       [(and their completions, by the previous rule)].  The child
       declarations occur after the declaration.

   10  If a body_stub is included, so is the corresponding subunit.

   11  If a type_declaration is included, then so is a corresponding
       record_representation_clause, if any.

 11.a   Reason:  This is so that the component_declarations can be
        directly visible in the record_representation_clause.

12   The declarative region of a declaration is also called the declarative
region of any view or entity declared by the declaration.

        12.a   Reason:  The constructs that have declarative regions are the
        constructs that can have declarations nested inside them.  Nested
        declarations are declared in that declarative region.  The one
        exception is for enumeration literals; although they are nested
        inside an enumeration type declaration, they behave as if they were
        declared at the same level as the type.

        12.b   To be honest:  A declarative region does not include parent_
        unit_names.

        12.c   Ramification:  A declarative region does not include context_
        clauses.

13   {occur immediately within} {immediately within} {within (immediately)}
{immediately enclosing} {enclosing (immediately)} A declaration occurs
immediately within a declarative region if this region is the innermost
declarative region that encloses the declaration (the immediately enclosing
declarative region), not counting the declarative region (if any) associated
with the declaration itself.

        13.a   Discussion:  Don't confuse the declarative region of a
        declaration with the declarative region in which it immediately
        occurs.

14   [{local to} A declaration is local to a declarative region if the
declaration occurs immediately within the declarative region.]

        14.a   Ramification:  That is, "occurs immediately within" and "local
        to" are synonyms (when referring to declarations).

[An entity is local to a declarative region if the entity is declared by a
declaration that is local to the declarative region.]

        14.b   Ramification:  Thus, ``local to'' applies to both declarations
        and entities, whereas ``occurs immediately within'' only applies to
        declarations.  We use this term only informally; for cases where
        precision is required, we use the term "occurs immediately within",
        since it is less likely to cause confusion.

15   {global to} A declaration is global to a declarative region if the
declaration occurs immediately within another declarative region that
encloses the declarative region.  An entity is global to a declarative region
if the entity is declared by a declaration that is global to the declarative
region.


     NOTES
16   (1) The children of a parent library unit are inside the parent's
     declarative region, even though they do not occur inside the parent's
     declaration or body.  This implies that one can use (for example) "P.Q"
     to refer to a child of P whose defining name is Q, and that after "use
     P;" Q can refer (directly) to that child.

17   (2) As explained above and in 10.1.1, ``Compilation Units - Library
     Units'', all library units are descendants of Standard, and so are
     contained in the declarative region of Standard.  They are not inside
     the declaration or body of Standard, but they are inside its declarative
     region.

18   (3) For a declarative region that comes in multiple parts, the text of
     the declarative region does not contain any text that might appear
     between the parts.  Thus, when a portion of a declarative region is said
     to extend from one place to another in the declarative region, the
     portion does not contain any text that might appear between the parts of
     the declarative region.

   18.a   Discussion:  It is necessary for the things that have a declarative
        region to include anything that contains declarations (except for
        enumeration type declarations).  This includes any declaration that
        has a profile (that is, subprogram_declaration, subprogram_body,
        entry_declaration, subprogram_renaming_declaration, formal_
        subprogram_declaration, access-to-subprogram type_declaration), any-
        thing that has a discriminant_part (that is, various kinds of type_
        declaration), anything that has a component_list (that is, record
        type_declaration and record extension type_declaration), and finally
        the declarations of task and protected units and packages.


                         Wording Changes From Ada 83

        18.b   It was necessary to extend Ada 83's definition of declarative
        region to take the following Ada 9X features into account:

         18.c  Child library units.

         18.d  Derived types/type extensions -- we need a declarative
               region for inherited components and also for new
               components.

         18.e  All the kinds of types that allow discriminants.

         18.f  Protected units.

         18.g  Entries that have bodies instead of accept statements.

         18.h  The choice_parameter_specification of an exception_
               handler.

         18.i  The formal parameters of access-to-subprogram types.

         18.j  Renamings-as-body.

        18.k   Discriminated and access-to-subprogram type declarations need
        a declarative region.  Enumeration type declarations cannot have one,
        because you don't have to say "Color.Red" to refer to the literal Red
        of Color.  For other type declarations, it doesn't really matter
        whether or not there is an associated declarative region, so for
        simplicity, we give one to all types except enumeration types.

        18.l   We now say that an accept_statement has its own declarative
        region, rather than being part of the declarative region of the
        entry_declaration, so that declarative regions are properly nested
        regions of text, so that it makes sense to talk about "inner
        declarative regions," and "...extends to the end of a declarative
        region."  Inside an accept_statement, the name of one of the
        parameters denotes the parameter_specification of the accept_
        statement, not that of the entry_declaration.  If the accept_
        statement is nested within a block_statement, these parameter_
        specifications can hide declarations of the block_statement.  The
        semantics of such cases was unclear in RM83.

        18.m   To be honest:  Unfortunately, we have the same problem for the
        entry name itself -- it should denote the accept_statement, but
        accept_statements are not declarations.  They should be, and they
        should hide the entry from all visibility within themselves.

        18.n   Note that we can't generalize this to entry_bodies, or other
        bodies, because the declarative_part of a body is not supposed to
        contain (explicit) homographs of things in the declaration.  It works
        for accept_statements only because an accept_statement does not have
        a declarative_part.

        18.o   To avoid confusion, we use the term ``local to'' only
        informally in Ada 9X.  Even RM83 used the term incorrectly (see, for
        example, RM83-12.3(13)).

        18.p   In Ada 83, (root) library units were inside Standard; it was
        not clear whether the declaration or body of Standard was meant.  In
        Ada 9X, they are children of Standard, and so occur immediately
        within Standard's declarative region, but not within either the
        declaration or the body.  (See RM83-8.6(2) and RM83-10.1.1(5).)



8.2 Scope of Declarations

1   [For each declaration, the language rules define a certain portion of the
program text called the scope of the declaration.  The scope of a declaration
is also called the scope of any view or entity declared by the declaration.
Within the scope of an entity, and only there, there are places where it is
legal to refer to the declared entity.  These places are defined by the rules
of visibility and overloading.]


                              Static Semantics

2   {immediate scope (of a declaration)} The immediate scope of a declaration
is a portion of the declarative region immediately enclosing the declaration.
The immediate scope starts at the beginning of the declaration, except in the
case of an overloadable declaration, in which case the immediate scope starts
just after the place where the profile of the callable entity is determined
(which is at the end of the _specification for the callable entity, or at the
end of the generic_instantiation if an instance).

        2.a   Reason:  The reason for making overloadable declarations with
        profiles special is to simplify compilation:  until the compiler has
        determined the profile, it doesn't know which other declarations are
        homographs of this one, so it doesn't know which ones this one should
        hide.  Without this rule, two passes over the _specification or
        generic_instantiation would be required to resolve names that denote
        things with the same name as this one.

The immediate scope extends to the end of the declarative region, with the
following exceptions:

    3  The immediate scope of a library_item includes only its semantic
       dependents.

 3.a    Reason:  Section 10 defines only a partial ordering of library_
        items.  Therefore, it is a good idea to restrict the immediate
        scope (and the scope, defined below) to semantic dependents.

 3.b    Consider also examples like this:

3.c         package P is end P;

3.d         package P.Q is
                I : Integer := 0;
            end P.Q;

3.e         with P;
            package R is
                package X renames P;
                X.Q.I := 17; -- Illegal!
            end R;

 3.f    The scope of P.Q does not contain R. Hence, neither P.Q nor X.Q
        are visible within R. However, the name R.X.Q would be visible
        in some other library unit where both R and P.Q are visible
        (assuming R were made legal by removing the offending
        declaration).

    4  The immediate scope of a declaration in the private part of a
       library unit does not include the visible part of any public
       descendant of that library unit.  {descendant [relationship with
       scope]}

 4.a    Ramification:  In other words, a declaration in the private part
        can be visible within the visible part, private part and body of
        a private child unit.  On the other hand, such a declaration can
        be visible within only the private part and body of a public
        child unit.

 4.b    Reason:  The purpose of this rule is to prevent children from
        giving private information to clients.

 4.c    Ramification:  For a public child subprogram, this means that
        the parent's private part is not visible in the formal_parts of
        the declaration and of the body.  This is true even for
        subprogram_bodies that are not completions.  For a public child
        generic unit, it means that the parent's private part is not
        visible in the generic_formal_part, as well as in the first list
        of basic_declarative_items (for a generic package), or the
        formal_part(s) (for a generic subprogram).

5   {visible part} [The visible part of (a view of) an entity is a portion of
the text of its declaration containing declarations that are visible from
outside.]  {private part [distributed]} The private part of (a view of) an
entity that has a visible part contains all declarations within the
declaration of (the view of) the entity, except those in the visible part;
[these are not visible from outside.  Visible and private parts are defined
only for these kinds of entities: callable entities, other program units, and
composite types.]

    6  {visible part [of a view of a callable entity]} The visible part
       of a view of a callable entity is its profile.

    7  {visible part [of a view of a composite type]} The visible part
       of a composite type other than a task or protected type consists
       of the declarations of all components declared [(explicitly or
       implicitly)] within the type_declaration.

    8  {visible part [of a generic unit]} The visible part of a generic
       unit includes the generic_formal_part.  For a generic package, it
       also includes the first list of basic_declarative_items of the
       package_specification.  For a generic subprogram, it also
       includes the profile.

 8.a    Reason:  Although there is no way to reference anything but the
        formals from outside a generic unit, they are still in the
        visible part in the sense that the corresponding declarations in
        an instance can be referenced (at least in some cases).  In
        other words, these declarations have an effect on the outside
        world.  The visible part of a generic unit needs to be defined
        this way in order to properly support the rule that makes a
        parent's private part invisible within a public child's visible
        part.

 8.b    Ramification:  The visible part of an instance of a generic unit
        is as defined for packages and subprograms; it is not defined in
        terms of the visible part of a generic unit.

    9  [The visible part of a package, task unit, or protected unit
       consists of declarations in the program unit's declaration other
       than those following the reserved word private, if any; see 7.1
       and 12.7 for packages, 9.1 for task units, and 9.4 for protected
       units.]

10   {scope (of a declaration)} The scope of a declaration always contains
the immediate scope of the declaration.  In addition, for a given declaration
that occurs immediately within the visible part of an outer declaration, or
is a public child of an outer declaration, the scope of the given declaration
extends to the end of the scope of the outer declaration, except that the
scope of a library_item includes only its semantic dependents.

        10.a   Ramification:  Note the recursion.  If a declaration appears
        in the visible part of a library unit, its scope extends to the end
        of the scope of the library unit, but since that only includes
        dependents of the declaration of the library unit, the scope of the
        inner declaration also only includes those dependents.  If X renames
        library package P, which has a child Q, a with_clause mentioning P.Q
        is necessary to be able to refer to X.Q, even if P.Q is visible at
        the place where X is declared.

11   {immediate scope (of (a view of) an entity)} The immediate scope of a
declaration is also the immediate scope of the entity or view declared by the
declaration.  {scope (of (a view of) an entity)} Similarly, the scope of a
declaration is also the scope of the entity or view declared by the
declaration.

        11.a   Ramification:  The rule for immediate scope implies the
        following:

         11.b  If the declaration is that of a library unit, then the
               immediate scope includes the declarative region of the
               declaration itself, but not other places, unless they are
               within the scope of a with_clause that mentions the
               library unit.

               11.c   It is necessary to attach the semantics of with_
               clauses to [immediate] scopes (as opposed to visibility),
               in order for various rules to work properly.  A library
               unit should hide a homographic implicit declaration that
               appears in its parent, but only within the scope of a
               with_clause that mentions the library unit.  Otherwise,
               we would violate the "legality determinable via semantic
               dependences" rule of Section 10, ``Program Structure and
               Compilation Issues''.  The declaration of a library unit
               should be allowed to be a homograph of an explicit
               declaration in its parent's body, so long as that body
               does not mention the library unit in a with_clause.

               11.d   This means that one cannot denote the declaration
               of the library unit, but one might still be able to
               denote the library unit via another view.

               11.e   A with_clause does not make the declaration of a
               library unit visible; the lack of a with_clause prevents
               it from being visible.  Even if a library unit is
               mentioned in a with_clause, its declaration can still be
               hidden.

         11.f  The completion of the declaration of a library unit
               (assuming that's also a declaration) is not visible,
               neither directly nor by selection, outside that
               completion.

         11.g  The immediate scope of a declaration immediately within
               the body of a library unit does not include any child of
               that library unit.

               11.h   This is needed to prevent children from looking
               inside their parent's body.  The children are in the
               declarative region of the parent, and they might be after
               the parent's body.  Therefore, the scope of a declaration
               that occurs immediately within the body might include
               some children.
     NOTES
12   (4) There are notations for denoting visible declarations that are not
     directly visible.  For example, parameter_specifications are in the
     visible part of a subprogram_declaration so that they can be used in
     named-notation calls appearing outside the called subprogram.  For
     another example, declarations of the visible part of a package can be
     denoted by expanded names appearing outside the package, and can be made
     directly visible by a use_clause.

   12.a   Ramification:  There are some obscure involving generics cases in
        which there is no such notation.  See Section 12.


                            Extensions to Ada 83

        12.b   {extensions to Ada 83} The fact that the immediate scope of an
        overloadable declaration does not include its profile is new to Ada
        9X.  It replaces RM83-8.3(16), which said that within a subprogram
        specification and within the formal part of an entry declaration or
        accept statement, all declarations with the same designator as the
        subprogram or entry were hidden from all visibility.  The
        RM83-8.3(16) rule seemed to be overkill, and created both
        implementation difficulties and unnecessary semantic complexity.

                         Wording Changes From Ada 83

        12.c   We no longer need to talk about the scope of notations,
        identifiers, character_literals, and operator_symbols.

        12.d   The notion of "visible part" has been extended in Ada 9X.  The
        syntax of task and protected units now allows private parts, thus
        requiring us to be able to talk about the visible part as well.  It
        was necessary to extend the concept to subprograms and to generic
        units, in order for the visibility rules related to child library
        units to work properly.  It was necessary to define the concept
        separately for generic formal packages, since their visible part is
        slightly different from that of a normal package.  Extending the
        concept to composite types made the definition of scope slightly
        simpler.  We define visible part for some things elsewhere, since it
        makes a big difference to the user for those things.  For composite
        types and subprograms, however, the concept is used only in arcane
        visibility rules, so we localize it to this clause.

        12.e   In Ada 83, the semantics of with_clauses was described in
        terms of visibility.  It is now described in terms of [immediate]
        scope.

        12.f   We have clarified that the following is illegal (where Q and R
        are library units):

12.g        package Q is
                I : Integer := 0;
            end Q;

12.h        package R is
                package X renames Standard;
                X.Q.I := 17; -- Illegal!
            end R;

        12.i   even though Q is declared in the declarative region of
        Standard, because R does not mention Q in a with_clause.



8.3 Visibility

1   [{visibility rules} The visibility rules, given below, determine which
declarations are visible and directly visible at each place within a program.
The visibility rules apply to both explicit and implicit declarations.]


                              Static Semantics

2   {visibility (direct)} {directly visible} {directly visible} A declaration
is defined to be directly visible at places where a name consisting of only
an identifier or operator_symbol is sufficient to denote the declaration;
that is, no selected_component notation or special context (such as preceding
=> in a named association) is necessary to denote the declaration.  {visible}
A declaration is defined to be visible wherever it is directly visible, as
well as at other places where some name (such as a selected_component) can
denote the declaration.

3   The syntactic category direct_name is used to indicate contexts where
direct visibility is required.  The syntactic category selector_name is used
to indicate contexts where visibility, but not direct visibility, is
required.

4   {visibility (immediate)} {visibility (use clause)} There are two kinds of
direct visibility:  immediate visibility and use-visibility.  {immediately
visible} A declaration is immediately visible at a place if it is directly
visible because the place is within its immediate scope.  {use-visible} A
declaration is use-visible if it is directly visible because of a use_clause
(see 8.4).  Both conditions can apply.

5   {hiding} A declaration can be hidden, either from direct visibility, or
from all visibility, within certain parts of its scope.  {hidden from all
visibility} Where hidden from all visibility, it is not visible at all
(neither using a direct_name nor a selector_name).  {hidden from direct
visibility} Where hidden from direct visibility, only direct visibility is
lost; visibility using a selector_name is still possible.

6   [{overloaded} Two or more declarations are overloaded if they all have
the same defining name and there is a place where they are all directly
visible.]

        6.a   Ramification:  Note that a name can have more than one possible
        interpretation even if it denotes a non-overloadable entity.  For
        example, if there are two functions F that return records, both
        containing a component called C, then the name F.C has two possible
        interpretations, even though component declarations are not
        overloadable.

7   {overloadable} The declarations of callable entities [(including
enumeration literals)] are overloadable[, meaning that overloading is allowed
for them].

        7.a   Ramification:  A generic_declaration is not overloadable within
        its own generic_formal_part.  This follows from the rules about when
        a name denotes a current instance.  See AI-00286.  This implies that
        within a generic_formal_part, outer declarations with the same
        defining name are hidden from direct visibility.  It also implies
        that if a generic formal parameter has the same defining name as the
        generic itself, the formal parameter hides the generic from direct
        visibility.

8   {homograph} Two declarations are homographs if they have the same
defining name, and, if both are overloadable, their profiles are type
conformant.  {type conformance [partial]}[An inner declaration hides any
outer homograph from direct visibility.]

9   [Two homographs are not generally allowed immediately within the same
declarative region unless one overrides the other (see Legality Rules
below).]  {override} A declaration overrides another homograph that occurs
immediately within the same declarative region in the following cases:

   10  An explicit declaration overrides an implicit declaration of a
       primitive subprogram, [regardless of which declaration occurs
       first];

 10.a   Ramification:  And regardless of whether the explicit
        declaration is overloadable or not.

 10.b   The ``regardless of which declaration occurs first'' is there
        because the explicit declaration could be a primitive subprogram
        of a partial view, and then the full view might inherit a
        homograph.  We are saying that the explicit one wins (within its
        scope), even though the implicit one comes later.

 10.c   If the overriding declaration is also a subprogram, then it is a
        primitive subprogram.

 10.d   As explained in 7.3.1, ``Private Operations'', some inherited
        primitive subprograms are never declared.  Such subprograms
        cannot be overridden, although they can be reached by
        dispatching calls in the case of a tagged type.

   11  The implicit declaration of an inherited operator overrides that
       of a predefined operator;

 11.a   Ramification:  In a previous version of Ada 9X, we tried to
        avoid the notion of predefined operators, and say that they were
        inherited from some magical root type.  However, this seemed
        like too much mechanism.  Therefore, a type can have a
        predefined "+" as well as an inherited "+".  The above rule says
        the inherited one wins.

 11.b   The ``regardless of which declaration occurs first'' applies
        here as well, in the case where derived_type_declaration in the
        visible part of a public library unit derives from a private
        type declared in the parent unit, and the full view of the
        parent type has additional predefined operators, as explained in
        7.3.1, ``Private Operations''.  Those predefined operators can
        be overridden by inherited subprograms implicitly declared
        earlier.

   12  An implicit declaration of an inherited subprogram overrides a
       previous implicit declaration of an inherited subprogram.

   13  [For an implicit declaration of a primitive subprogram in a
       generic unit, there is a copy of this declaration in an
       instance.]  However, a whole new set of primitive subprograms is
       implicitly declared for each type declared within the visible
       part of the instance.  These new declarations occur immediately
       after the type declaration, and override the copied ones.  [The
       copied ones can be called only from within the instance; the new
       ones can be called only from outside the instance, although for
       tagged types, the body of a new one can be executed by a call to
       an old one.]

 13.a   Discussion:  In addition, this is also stated redundantly
        (again), and is repeated, in 12.3, ``Generic Instantiation''.
        The rationale for the rule is explained there.

14   {visible} {hidden from all visibility [distributed]} A declaration is
visible within its scope, except where hidden from all visibility, as
follows:

   15  {hidden from all visibility [for overridden declaration]} An
       overridden declaration is hidden from all visibility within the
       scope of the overriding declaration.
 15.a   Ramification:  We have to talk about the scope of the overriding
        declaration, not its visibility, because it hides even when it
        is itself hidden.

 15.b   Note that the scope of an explicit subprogram_declaration does
        not start until after its profile.

   16  {hidden from all visibility [within the declaration itself]} A
       declaration is hidden from all visibility until the end of the
       declaration, except:

          17  For a record type or record extension, the declaration is
              hidden from all visibility only until the reserved word
              record;

          18  For a package_declaration, task declaration, protected
              declaration, generic_package_declaration, or subprogram_
              body, the declaration is hidden from all visibility only
              until the reserved word is of the declaration.
              {94-4942.a}

 18.a   Ramification:  We're talking about the is of the construct
        itself, here, not some random is that might appear in a generic_
        formal_part.

   19  {hidden from all visibility [for a declaration completed by a
       subsequent declaration]} If the completion of a declaration is a
       declaration, then within the scope of the completion, the first
       declaration is hidden from all visibility.  Similarly, a
       discriminant_specification or parameter_specification is hidden
       within the scope of a corresponding discriminant_specification or
       parameter_specification of a corresponding completion, or of a
       corresponding accept_statement.

 19.a   Ramification:  This rule means, for example, that within the
        scope of a full_type_declaration that completes a private_type_
        declaration, the name of the type will denote the full_type_
        declaration, and therefore the full view of the type.  On the
        other hand, if the completion is not a declaration, then it
        doesn't hide anything, and you can't denote it.

   20  {hidden from all visibility [by lack of a with_clause]} The
       declaration of a library unit (including a library_unit_renaming_
       declaration) is hidden from all visibility except at places that
       are within its declarative region or within the scope of a with_
       clause that mentions it.  [For each declaration or renaming of a
       generic unit as a child of some parent generic package, there is
       a corresponding declaration nested immediately within each
       instance of the parent.]  Such a nested declaration is hidden
       from all visibility except at places that are within the scope of
       a with_clause that mentions the child.  {94-4933.a}

 20.a   Discussion:  This is the rule that prevents with_clauses from
        being transitive; the [immediate] scope includes indirect
        semantic dependents.

21   {directly visible} {immediately visible} {visibility (direct)}
{visibility (immediate)} A declaration with a defining_identifier or
defining_operator_symbol is immediately visible [(and hence directly
visible)] within its immediate scope {hidden from direct visibility
[distributed]} except where hidden from direct visibility, as follows:

   22  {hidden from direct visibility [by an inner homograph]} A
       declaration is hidden from direct visibility within the immediate
       scope of a homograph of the declaration, if the homograph occurs
       within an inner declarative region;

   23  {hidden from direct visibility [where hidden from all
       visibility]} A declaration is also hidden from direct visibility
       where hidden from all visibility.


                            Name Resolution Rules

24   {possible interpretation [for direct_names]} A direct_name shall resolve
to denote a directly visible declaration whose defining name is the same as
the direct_name.  {possible interpretation [for selector_names]} A selector_
name shall resolve to denote a visible declaration whose defining name is the
same as the selector_name.

        24.a   Discussion:  "The same as" has the obvious meaning here, so
        for +, the possible interpretations are declarations whose defining
        name is "+" (an operator_symbol).

25   These rules on visibility and direct visibility do not apply in a
context_clause, a parent_unit_name, or a pragma that appears at the place of
a compilation_unit.  For those contexts, see the rules in 10.1.6,
``Environment-Level Visibility Rules''.

        25.a   Ramification:  Direct visibility is irrelevant for character_
        literals.  In terms of overload resolution character_literals are
        similar to other literals, like null -- see 4.2.  For character_
        literals, there is no need to worry about hiding, since there is no
        way to declare homographs.


                               Legality Rules

26   An explicit declaration is illegal if there is a homograph occurring
immediately within the same declarative region that is visible at the place
of the declaration, and is not hidden from all visibility by the explicit
declaration.  Similarly, the context_clause for a subunit is illegal if it
mentions (in a with_clause) some library unit, and there is a homograph of
the library unit that is visible at the place of the corresponding stub, and
the homograph and the mentioned library unit are both declared immediately
within the same declarative region.  {generic contract issue [partial]} These
rules also apply to dispatching operations declared in the visible part of an
instance of a generic unit.  However, they do not apply to other overloadable
declarations in an instance[; such declarations may have type conformant
profiles in the instance, so long as the corresponding declarations in the
generic were not type conformant].  {type conformance [partial]}

        26.a   Discussion:  Normally, these rules just mean you can't
        explicitly declare two homographs immediately within the same
        declarative region.  The wording is designed to handle the following
        special cases:

         26.b  If the second declaration completes the first one, the
               second declaration is legal.

         26.c  If the body of a library unit contains an explicit
               homograph of a child of that same library unit, this is
               illegal only if the body mentions the child in its
               context_clause, or if some subunit mentions the child.
               Here's an example:

26.d               package P is
                   end P;

26.e               package P.Q is
                   end P.Q;

26.f               package body P is
                       Q : Integer; -- OK; we cannot see package P.Q here.
                       procedure Sub is separate;
                   end P;

26.g               with P.Q;
                   separate(P)
                   procedure Sub is -- Illegal.
                   begin
                       null;
                   end Sub;

               26.h   If package body P said "with P.Q;", then it would
               be illegal to declare the homograph Q: Integer.  But it
               does not, so the body of P is OK.  However, the subunit
               would be able to see both P.Q's, and is therefore
               illegal.

               26.i   A previous version of Ada 9X allowed the subunit,
               and said that references to P.Q would tend to be
               ambiguous.  However, that was a bad idea, because it
               requires overload resolution to resolve references to
               directly visible non-overloadable homographs, which is
               something compilers have never before been required to
               do.

        26.j   Note that we need to be careful which things we make "hidden
        from all visibility" versus which things we make simply illegal for
        names to denote.  The distinction is subtle.  The rules that disallow
        names denoting components within a type declaration (see 3.7) do not
        make the components invisible at those places, so that the above rule
        makes components with the same name illegal.  The same is true for
        the rule that disallows names denoting formal parameters within a
        formal_part (see 6.1).

        26.k   Discussion:  The part about instances is from AI-00012.  The
        reason it says ``overloadable declarations'' is because we don't want
        it to apply to type extensions that appear in an instance; components
        are not overloadable.


     NOTES
27   (5) Visibility for compilation units follows from the definition of the
     environment in 10.1.4, except that it is necessary to apply a with_
     clause to obtain visibility to a library_unit_declaration or library_
     unit_renaming_declaration.

28   (6) In addition to the visibility rules given above, the meaning of the
     occurrence of a direct_name or selector_name at a given place in the
     text can depend on the overloading rules (see 8.6).  {94-4666.a}

29   (7) Not all contexts where an identifier, character_literal, or
     operator_symbol are allowed require visibility of a corresponding
     declaration.  Contexts where visibility is not required are identified
     by using one of these three syntactic categories directly in a syntax
     rule, rather than using direct_name or selector_name.

   29.a   Ramification:  An identifier, character_literal or operator_symbol
        that occurs in one of the following contexts is not required to
        denote a visible or directly visible declaration:

         29.b  A defining name.

         29.c  The identifiers or operator_symbol that appear after the
               reserved word end in a proper_body.  Similarly for ``end
               loop'', etc.

         29.d  An attribute_designator.

         29.e  A pragma identifier.

         29.f  A pragma_argument_identifier.

         29.g  An identifier specific to a pragma used in a pragma
               argument.

   29.h   The visibility rules have nothing to do with the above cases; the
        meanings of such things are defined elsewhere.  Reserved words are
        not identifiers; the visibility rules don't apply to them either.

   29.i   Because of the way we have defined "declaration", it is possible
        for a usage name to denote a subprogram_body, either within that
        body, or (for a non-library unit) after it (since the body hides the
        corresponding declaration, if any).  Other bodies do not work that
        way.  Completions of type_ and deferred_constant_declarations do work
        that way.  Accept_statements are never denoted, although the
        parameter_specifications in their profiles can be.

   29.j   The scope of a subprogram does not start until after its profile.
        Thus, the following is legal:

29.k        X : constant Integer := 17;
            ...
            package P is
                procedure X(Y : in Integer := X);
            end P;

   29.l   The body of the subprogram will probably be illegal, however, since
        the constant X will be hidden by then.

   29.m   The rule is different for generic subprograms, since they are not
        overloadable; the following is illegal:

29.n        X : constant Integer := 17;
            package P is
                generic
                  Z : Integer := X; -- Illegal!
                procedure X(Y : in Integer := X); -- Illegal!
            end P;

        {94-4942.a}

   29.o   The constant X is hidden from direct visibility by the generic
        declaration.


                            Extensions to Ada 83

        29.p   {extensions to Ada 83} Declarations with the same defining
        name as that of a subprogram or entry being defined are nevertheless
        visible within the subprogram specification or entry declaration.

                         Wording Changes From Ada 83

        29.q   The term ``visible by selection'' is no longer defined.  We
        use the terms ``directly visible'' and ``visible'' (among other
        things).  There are only two regions of text that are of interest,
        here: the region in which a declaration is visible, and the region in
        which it is directly visible.

        29.r   Visibility is defined only for declarations.



8.4 Use Clauses

1   [A use_package_clause achieves direct visibility of declarations that
appear in the visible part of a package; a use_type_clause achieves direct
visibility of the primitive operators of a type.]


                         Language Design Principles

        1.a   {equivalence of use_clauses and selected_components} If and
        only if the visibility rules allow P.A, "use P;" should make A
        directly visible (barring name conflicts).  This means, for example,
        that child library units, and generic formals of a formal package
        whose formal_package_actual_part is (<>), should be made visible by a
        use_clause for the appropriate package.

        1.b   {Beaujolais effect} The rules for use_clauses were carefully
        constructed to avoid so-called Beaujolais effects, where the addition
        or removal of a single use_clause, or a single declaration in a
        "use"d package, would change the meaning of a program from one legal
        interpretation to another.

                                   Syntax

2   use_clause ::= use_package_clause | use_type_clause

3   use_package_clause ::= use package_name {, package_name};

4   use_type_clause ::= use type subtype_mark {, subtype_mark};


                               Legality Rules

5   A package_name of a use_package_clause shall denote a package.

        5.a   Ramification:  This includes formal packages.


                              Static Semantics

6   {scope (of a use_clause)} For each use_clause, there is a certain region
of text called the scope of the use_clause.  For a use_clause within a
context_clause of a library_unit_declaration or library_unit_renaming_
declaration, the scope is the entire declarative region of the declaration.
For a use_clause within a context_clause of a body, the scope is the entire
body [and any subunits (including multiply nested subunits).  The scope does
not include context_clauses themselves.]

7   For a use_clause immediately within a declarative region, the scope is
the portion of the declarative region starting just after the use_clause and
extending to the end of the declarative region.  However, the scope of a use_
clause in the private part of a library unit does not include the visible
part of any public descendant of that library unit.

        7.a   Reason:  The exception echoes the similar exception for
        ``immediate scope (of a declaration)'' (see 8.2).  It makes use_
        clauses work like this:

7.b         package P is
                type T is range 1..10;
            end P;

7.c         with P;
            package Parent is
            private
                use P;
                X : T;
            end Parent;

7.d         package Parent.Child is
                Y : T; -- Illegal!
                Z : P.T;
            private
                W : T;
            end Parent.Child;

        7.e   The declaration of Y is illegal because the scope of the ``use
        P'' does not include that place, so T is not directly visible there.
        The declarations of X, Z, and W are legal.

8   {potentially use-visible} For each package denoted by a package_name of a
use_package_clause whose scope encloses a place, each declaration that occurs
immediately within the declarative region of the package is potentially
use-visible at this place if the declaration is visible at this place.
{94-4666.b} For each type T or T'Class determined by a subtype_mark of a use_
type_clause whose scope encloses a place, the declaration of each primitive
operator of type T is potentially use-visible at this place if its
declaration is visible at this place.

        8.a   Ramification:  Primitive subprograms whose defining name is an
        identifier are not made potentially visible by a use_type_clause.  A
        use_type_clause is only for operators.

        8.b   The semantics described here should be similar to the semantics
        for expanded names given in 4.1.3, ``Selected Components'' so as to
        achieve the effect requested by the ``principle of equivalence of
        use_clauses and selected_components.''  Thus, child library units and
        generic formal parameters of a formal package are potentially
        use-visible when their enclosing package is use'd.

        8.c   The "visible at that place" part implies that applying a use_
        clause to a parent unit does not make all of its children use-visible
        -- only those that have been made visible by a with_clause.  It also
        implies that we don't have to worry about hiding in the definition of
        "directly visible" -- a declaration cannot be use-visible unless it
        is visible.

        8.d   Note that "use type T'Class;" is equivalent to "use type T;",
        which helps avoid breaking the generic contract model.

9   {use-visible} {visibility (use clause)} A declaration is use-visible if
it is potentially use-visible, except in these naming-conflict cases:

   10  A potentially use-visible declaration is not use-visible if the
       place considered is within the immediate scope of a homograph of
       the declaration.

   11  Potentially use-visible declarations that have the same
       identifier are not use-visible unless each of them is an
       overloadable declaration.

 11.a   Ramification:  Overloadable declarations don't cancel each other
        out, even if they are homographs, though if they are not
        distinguishable by formal parameter names or the presence or
        absence of default_expressions, any use will be ambiguous.  We
        only mention identifiers here, because declarations named by
        operator_symbols are always overloadable, and hence never cancel
        each other.  Direct visibility is irrelevant for character_
        literals.
                              Dynamic Semantics

12   {elaboration [use_clause]} The elaboration of a use_clause has no
effect.


                                  Examples

13   Example of a use clause in a context clause:

14  with Ada.Calendar; use Ada;

15   Example of a use type clause:

16  use type Rational_Numbers.Rational; -- see 7.1
    Two_Thirds: Rational_Numbers.Rational := 2/3;

{94-4774.c}

        16.a   Ramification:  In ``use X, Y;'', Y cannot refer to something
        made visible by the ``use'' of X. Thus, it's not (quite) equivalent
        to ``use X; use Y;''.

        16.b   If a given declaration is already immediately visible, then a
        use_clause that makes it potentially use-visible has no effect.
        Therefore, a use_type_clause for a type whose declaration appears in
        a place other than the visible part of a package has no effect; it
        cannot make a declaration use-visible unless that declaration is
        already immediately visible.

        16.c   "Use type S1;" and "use type S2;" are equivalent if S1 and S2
        are both subtypes of the same type.  In particular, "use type S;" and
        "use type S'Base;" are equivalent.

        16.d   Reason:  We considered adding a rule that prevented several
        declarations of views of the same entity that all have the same
        semantics from cancelling each other out.  For example, if a
        (possibly implicit) subprogram_declaration for "+" is potentially
        use-visible, and a fully conformant renaming of it is also
        potentially use-visible, then they (annoyingly) cancel each other
        out; neither one is use-visible.  The considered rule would have made
        just one of them use-visible.  We gave up on this idea due to the
        complexity of the rule.  It would have had to account for both
        overloadable and non-overloadable renaming_declarations, the case
        where the rule should apply only to some subset of the declarations
        with the same defining name, and the case of subtype_declarations
        (since they are claimed to be sufficient for renaming of subtypes).


                            Extensions to Ada 83

        16.e   {extensions to Ada 83} The use_type_clause is new to Ada 9X.

                         Wording Changes From Ada 83

        16.f   The phrase ``omitting from this set any packages that enclose
        this place'' is no longer necessary to avoid making something visible
        outside its scope, because we explicitly state that the declaration
        has to be visible in order to be potentially use-visible.



8.5 Renaming Declarations

1   [A renaming_declaration declares another name for an entity, such as an
object, exception, package, subprogram, entry, or generic unit.
Alternatively, a subprogram_renaming_declaration can be the completion of a
previous subprogram_declaration.]


                                   Syntax

2   renaming_declaration ::=
          object_renaming_declaration
        | exception_renaming_declaration
        | package_renaming_declaration
        | subprogram_renaming_declaration
        | generic_renaming_declaration


                              Dynamic Semantics

3   {elaboration [renaming_declaration]} The elaboration of a renaming_
declaration evaluates the name that follows the reserved word renames and
thereby determines the view and entity denoted by this name {renamed view}
{renamed entity} (the renamed view and renamed entity).  [A name that denotes
the renaming_declaration denotes (a new view of) the renamed entity.]


     NOTES
4    (8) Renaming may be used to resolve name conflicts and to act as a
     shorthand.  Renaming with a different identifier or operator_symbol does
     not hide the old name; the new name and the old name need not be visible
     at the same places.

5    (9) A task or protected object that is declared by an explicit object_
     declaration can be renamed as an object.  However, a single task or
     protected object cannot be renamed since the corresponding type is
     anonymous (meaning it has no nameable subtypes).  For similar reasons,
     an object of an anonymous array or access type cannot be renamed.

6    (10) A subtype defined without any additional constraint can be used to
     achieve the effect of renaming another subtype (including a task or
     protected subtype) as in

7        subtype Mode is Ada.Text_IO.File_Mode;


                         Wording Changes From Ada 83

        7.a   The second sentence of RM83-8.5(3), ``At any point where a
        renaming declaration is visible, the identifier, or operator symbol
        of this declaration denotes the renamed entity.''  is incorrect.  It
        doesn't say directly visible.  Also, such an identifier might resolve
        to something else.

        7.b   The verbiage about renamings being legal ``only if exactly
        one...'', which appears in RM83-8.5(4) (for objects) and RM83-8.5(7)
        (for subprograms) is removed, because it follows from the normal
        rules about overload resolution.  For language lawyers, these facts
        are obvious; for programmers, they are irrelevant, since failing
        these tests is highly unlikely.



8.5.1 Object Renaming Declarations

1   [An object_renaming_declaration is used to rename an object.]


                                   Syntax

2   object_renaming_declaration ::= defining_identifier : subtype_mark renames \
object_name;


                            Name Resolution Rules

3   The type of the object_name shall resolve to the type determined by the
subtype_mark.  {94-4500.a} {94-4505.a} {94-4506.a} {94-4507.a} {94-4509.a}
{94-4532.a}

        3.a   Reason:  A previous version of Ada 9X used the usual ``expected
        type'' wording:  ``The expected type for the object_name is that
        determined by the subtype_mark.''  We changed it so that this would
        be illegal:

3.b         X: T;
            Y: T'Class renames X; -- Illegal!

        3.c   When the above was legal, it was unclear whether Y was of type
        T or T'Class.  Note that we still allow this:

3.d         Z: T'Class := ...;
            W: T renames F(Z);

        3.e   where F is a function with a controlling parameter and result.
        This is admittedly a bit odd.

        3.f   Note that the matching rule for generic formal parameters of
        mode in out was changed to keep it consistent with the rule for
        renaming.  That makes the rule different for in vs. in out.

{94-5001.h}


                               Legality Rules

4   The renamed entity shall be an object.

5   The renamed entity shall not be a subcomponent that depends on
discriminants of a variable whose nominal subtype is unconstrained, unless
this subtype is indefinite, or the variable is aliased.  A slice of an array
shall not be renamed if this restriction disallows renaming of the array.

        5.a   Reason:  This prevents renaming of subcomponents that might
        disappear, which might leave dangling references.  Similar
        restrictions exist for the Access attribute.

        5.b   Implementation Note:  Note that if an implementation chooses to
        deallocate-then-reallocate on assignment_statements assigning to
        unconstrained definite objects, then it cannot represent renamings
        and access values as simple addresses, because the above rule does
        not apply to all components of such an object.

        5.c   Ramification:  If it is a generic formal object, then the
        assume-the-best or assume-the-worst rules are applied as appropriate.


                              Static Semantics

6   An object_renaming_declaration declares a new view [of the renamed
object] whose properties are identical to those of the renamed view.  [Thus,
the properties of the renamed object are not affected by the renaming_
declaration.  In particular, its value and whether or not it is a constant
are unaffected; similarly, the constraints that apply to an object are not
affected by renaming (any constraint implied by the subtype_mark of the
object_renaming_declaration is ignored).]

        6.a   Discussion:  Because the constraints are ignored, it is a good
        idea to use the nominal subtype of the renamed object when writing an
        object_renaming_declaration.


                                  Examples

7   Example of renaming an object:

8   declare
       L : Person renames Leftmost_Person; -- see 3.10.1
    begin
       L.Age := L.Age + 1;
    end;


                         Wording Changes From Ada 83

        8.a   The phrase ``subtype ... as defined in a corresponding object
        declaration, component declaration, or component subtype indica-
        tion,'' from RM83-8.5(5), is incorrect in Ada 9X; therefore we
        removed it.  It is incorrect in the case of an object with an
        indefinite unconstrained nominal subtype.



8.5.2 Exception Renaming Declarations

1   [An exception_renaming_declaration is used to rename an exception.]


                                   Syntax

2   exception_renaming_declaration ::= defining_identifier : exception renames \
exception_name;


                               Legality Rules

3   The renamed entity shall be an exception.


                              Static Semantics

4   An exception_renaming_declaration declares a new view [of the renamed
exception].


                                  Examples

5   Example of renaming an exception:

6   EOF : exception renames Ada.IO_Exceptions.End_Error;-- see A.13



8.5.3 Package Renaming Declarations

1   [A package_renaming_declaration is used to rename a package.]


                                   Syntax

2   package_renaming_declaration ::= package defining_program_unit_name renames\
 package_name;


                               Legality Rules

3   The renamed entity shall be a package.


                              Static Semantics

4   A package_renaming_declaration declares a new view [of the renamed
package].


                                  Examples

5   Example of renaming a package:

6   package TM renames Table_Manager;



8.5.4 Subprogram Renaming Declarations

1   A subprogram_renaming_declaration can serve as the completion of a
subprogram_declaration; {renaming-as-body} such a renaming_declaration is
called a renaming-as-body.  {renaming-as-declaration} A subprogram_renaming_
declaration that is not a completion is called a renaming-as-declaration[,
and is used to rename a subprogram (possibly an enumeration literal) or an
entry].

        1.a   Ramification:  A renaming-as-body is a declaration, as defined
        in Section 3.


                                   Syntax

2   subprogram_renaming_declaration ::= subprogram_specification renames callab\
le_entity_name;


                            Name Resolution Rules

3   {expected profile [subprogram_renaming_declaration]} The expected profile
for the callable_entity_name is the profile given in the subprogram_
specification.


                               Legality Rules

4   The profile of a renaming-as-declaration shall be mode-conformant with
that of the renamed callable entity.  {mode conformance (required)}

5   The profile of a renaming-as-body shall be subtype-conformant with that
of the renamed callable entity, and shall conform fully to that of the
declaration it completes.  {subtype conformance (required)} {full conformance
(required)} If the renaming-as-body completes that declaration before the
subprogram it declares is frozen, the subprogram it declares takes its
convention from the renamed subprogram; otherwise the convention of the
renamed subprogram shall not be Intrinsic.  {94-4774.b}

        5.a   Reason:  The first part of the first sentence is to allow an
        implementation of a renaming-as-body as a single jump instruction to
        the target subprogram.  Among other things, this prevents a
        subprogram from being completed with a renaming of an entry.  (In
        most cases, the target of the jump can be filled in at link time.  In
        some cases, such as a renaming of a name like "A(I).all", an indirect
        jump is needed.  Note that the name is evaluated at renaming time,
        not at call time.)

        5.b   The second part of the first sentence is the normal rule for
        completions of subprogram_declarations.

        5.c   Ramification:  An entry_declaration, unlike a subprogram_
        declaration, cannot be completed with a renaming_declaration.  Nor
        can a generic_subprogram_declaration.

        5.d   The syntax rules prevent a protected subprogram declaration
        from being completed by a renaming.  This is fortunate, because it
        allows us to avoid worrying about whether the implicit protected
        object parameter of a protected operation is involved in the
        conformance rules.

6   A name that denotes a formal parameter of the subprogram_specification is
not allowed within the callable_entity_name.

        6.a   Reason:  This is to prevent things like this:

6.b         function F(X : Integer) return Integer renames Table(X).all;

        6.c   A similar rule in 6.1 forbids things like this:

6.d         function F(X : Integer; Y : Integer := X) return Integer;


                              Static Semantics

7   A renaming-as-declaration declares a new view of the renamed entity.  The
profile of this new view takes its subtypes, parameter modes, and calling
convention from the original profile of the callable entity, while taking the
formal parameter names and default_expressions from the profile given in the
subprogram_renaming_declaration.  The new view is a function or procedure,
never an entry.

        7.a   To be honest:  When renaming an entry as a procedure, the
        compile-time rules apply as if the new view is a procedure, but the
        run-time semantics of a call are that of an entry call.

        7.b   Ramification:  For example, it is illegal for the entry_call_
        statement of a timed_entry_call to call the new view.  But what looks
        like a procedure call will do things like barrier waiting.


                              Dynamic Semantics

8   For a call on a renaming of a dispatching subprogram that is overridden,
if the overriding occurred before the renaming, then the body executed is
that of the overriding declaration, even if the overriding declaration is not
visible at the place of the renaming; otherwise, the inherited or predefined
subprogram is called.

        8.a   Discussion:  Note that whether or not the renaming is itself
        primitive has nothing to do with the renamed subprogram.

        8.b   Note that the above rule is only for tagged types.

        8.c   Consider the following example:

8.d         package P is
                type T is tagged null record;
                function Predefined_Equal(X, Y : T) return Boolean renames "=";
            private
                function "="(X, Y : T) return Boolean; -- Override predefined "\
=".
            end P;

8.e         with P; use P;
            package Q is
                function User_Defined_Equal(X, Y : T) return Boolean renames P.\
"=";
            end Q;

        8.f   A call on Predefined_Equal will execute the predefined equality
        operator of T, whereas a call on User_Defined_Equal will execute the
        body of the overriding declaration in the private part of P.

        8.g   Thus a renaming allows one to squirrel away a copy of an
        inherited or predefined subprogram before later overriding it.
        {squirrel away (included in fairness to alligators)}


     NOTES
9    (11) A procedure can only be renamed as a procedure.  A function whose
     defining_designator is either an identifier or an operator_symbol can be
     renamed with either an identifier or an operator_symbol; for renaming as
     an operator, the subprogram specification given in the renaming_
     declaration is subject to the rules given in 6.6 for operator
     declarations.  Enumeration literals can be renamed as functions;
     similarly, attribute_references that denote functions (such as
     references to Succ and Pred) can be renamed as functions.  An entry can
     only be renamed as a procedure; the new name is only allowed to appear
     in contexts that allow a procedure name.  An entry of a family can be
     renamed, but an entry family cannot be renamed as a whole.

10   (12) The operators of the root numeric types cannot be renamed because
     the types in the profile are anonymous, so the corresponding
     specifications cannot be written; the same holds for certain attributes,
     such as Pos.  {94-4666.c}

11   (13) Calls with the new name of a renamed entry are procedure_call_
     statements and are not allowed at places where the syntax requires an
     entry_call_statement in conditional_ and timed_entry_calls, nor in an
     asynchronous_select; similarly, the Count attribute is not available for
     the new name.

12   (14) The primitiveness of a renaming-as-declaration is determined by its
     profile, and by where it occurs, as for any declaration of (a view of) a
     subprogram; primitiveness is not determined by the renamed view.  In
     order to perform a dispatching call, the subprogram name has to denote a
     primitive subprogram, not a non-primitive renaming of a primitive
     subprogram.

   12.a   Reason:  A subprogram_renaming_declaration could more properly be
        called renaming_as_subprogram_declaration, since you're renaming
        something as a subprogram, but you're not necessarily renaming a
        subprogram.  But that's too much of a mouthful.  Or, alternatively,
        we could call it a callable_entity_renaming_declaration, but that's
        even worse.  Not only is it a mouthful, it emphasizes the entity
        being renamed, rather than the new view, which we think is a bad
        idea.  We'll live with the oddity.


                                  Examples

13   Examples of subprogram renaming declarations:

14  procedure My_Write(C : in Character) renames Pool(K).Write; --  see 4.1.3

15  function Real_Plus(Left, Right : Real   ) return Real    renames "+";
    function Int_Plus (Left, Right : Integer) return Integer renames "+";

16  function Rouge return Color renames Red;  --  see 3.5.1
    function Rot   return Color renames Red;
    function Rosso return Color renames Rouge;

17  function Next(X : Color) return Color renames Color'Succ; -- see 3.5.1

18   Example of a subprogram renaming declaration with new parameter names:

19  function "*" (X,Y : Vector) return Real renames Dot_Product; -- see 6.1

20   Example of a subprogram renaming declaration with a new default
expression:

21  function Minimum(L : Link := Head) return Cell renames Min_Cell; -- see 6.1



8.5.5 Generic Renaming Declarations

1   [A generic_renaming_declaration is used to rename a generic unit.]


                                   Syntax

2   generic_renaming_declaration ::=
        generic package       defining_program_unit_name renames generic_packag\
e_name;
      | generic procedure     defining_program_unit_name renames generic_proced\
ure_name;
      | generic function      defining_program_unit_name renames generic_functi\
on_name;


                               Legality Rules

3   The renamed entity shall be a generic unit of the corresponding kind.


                              Static Semantics

4   A generic_renaming_declaration declares a new view [of the renamed
generic unit].


     NOTES
5    (15) Although the properties of the new view are the same as those of
     the renamed view, the place where the generic_renaming_declaration
     occurs may affect the legality of subsequent renamings and
     instantiations that denote the generic_renaming_declaration, in
     particular if the renamed generic unit is a library unit (see 10.1.1).


                                  Examples

6   Example of renaming a generic unit:

7   generic package Enum_IO renames Ada.Text_IO.Enumeration_IO;  -- see A.10.10


                            Extensions to Ada 83

        7.a   {extensions to Ada 83} Renaming of generic units is new to Ada
        9X.  It is particularly important for renaming child library units
        that are generic units.  For example, it might be used to rename
        Numerics.Generic_Elementary_Functions as simply Generic_Elementary_
        Functions, to match the name for the corresponding Ada-83-based
        package.

                         Wording Changes From Ada 83

        7.b   The information in RM83-8.6, ``The Package Standard,'' has been
        updated for the child unit feature, and moved to Annex A, except for
        the definition of ``predefined type,'' which has been moved to 3.2.1.



8.6 The Context of Overload Resolution

1   [{overload resolution} Because declarations can be overloaded, it is
possible for an occurrence of a usage name to have more than one possible
interpretation; in most cases, ambiguity is disallowed.  This clause
describes how the possible interpretations resolve to the actual
interpretation.

2   {overloading rules} Certain rules of the language (the Name Resolution
Rules) are considered ``overloading rules''.  If a possible interpretation
violates an overloading rule, it is assumed not to be the intended
interpretation; some other possible interpretation is assumed to be the
actual interpretation.  On the other hand, violations of non-overloading
rules do not affect which interpretation is chosen; instead, they cause the
construct to be illegal.  To be legal, there usually has to be exactly one
acceptable interpretation of a construct that is a ``complete context'', not
counting any nested complete contexts.

3   {grammar (resolution of ambiguity)} The syntax rules of the language and
the visibility rules given in 8.3 determine the possible interpretations.
Most type checking rules (rules that require a particular type, or a
particular class of types, for example) are overloading rules.  Various rules
for the matching of formal and actual parameters are overloading rules.]


                         Language Design Principles

        3.a   The type resolution rules are intended to minimize the need for
        implicit declarations and preference rules associated with implicit
        conversion and dispatching operations.

                            Name Resolution Rules

4   {complete context} [Overload resolution is applied separately to each
complete context, not counting inner complete contexts.]  Each of the
following constructs is a complete context:

    5  A context_item.

    6  A declarative_item or declaration.

 6.a    Ramification:  A loop_parameter_specification is a declaration,
        and hence a complete context.

    7  A statement.

    8  A pragma_argument_association.

 8.a    Reason:  We would make it the whole pragma, except that certain
        pragma arguments are allowed to be ambiguous, and ambiguity
        applies to a complete context.

    9  The expression of a case_statement.

 9.a    Ramification:  This means that the expression is resolved
        without looking at the choices.

10   {interpretation (of a complete context)} {overall interpretation (of a
complete context)} An (overall) interpretation of a complete context embodies
its meaning, and includes the following information about the constituents of
the complete context, not including constituents of inner complete contexts:

   11  for each constituent of the complete context, to which syntactic
       categories it belongs, and by which syntax rules; and

 11.a   Ramification:  Syntactic categories is plural here, because
        there are lots of trivial productions -- an expression might
        also be all of the following, in this order: identifier, name,
        primary, factor, term, simple_expression, and relation.
        Basically, we're trying to capture all the information in the
        parse tree here, without using compiler-writer's jargon like
        ``parse tree''.

   12  for each usage name, which declaration it denotes (and,
       therefore, which view and which entity it denotes); and

 12.a   Ramification:  In most cases, a usage name denotes the view
        declared by the denoted declaration.  However, in certain cases,
        a usage name that denotes a declaration and appears inside the
        declarative region of that same declaration, denotes the current
        instance of the declaration.  For example, within a task_body, a
        usage name that denotes the task_type_declaration denotes the
        object containing the currently executing task, and not the task
        type declared by the declaration.

   13  for a complete context that is a declarative_item, whether or not
       it is a completion of a declaration, and (if so) which
       declaration it completes.

        13.a   Ramification:  Unfortunately, we are not confident that the
        above list is complete.  We'll have to live with that.

        13.b   To be honest:  For ``possible'' interpretations, the above
        information is tentative.

        13.c   Discussion:  A possible interpretation (an input to overload
        resolution) contains information about what a usage name might
        denote, but what it actually does denote requires overload resolution
        to determine.  Hence the term ``tentative'' is needed for possible
        interpretations; otherwise, the definition would be circular.

14   {possible interpretation} A possible interpretation is one that obeys
the syntax rules and the visibility rules.  {acceptable interpretation}
{resolve (overload resolution)} {interpretation (overload resolution)} An
acceptable interpretation is a possible interpretation that obeys the
overloading rules[, that is, those rules that specify an expected type or
expected profile, or specify how a construct shall resolve or be
interpreted.]

        14.a   To be honest:  One rule that falls into this category, but
        does not use the above-mentioned magic words, is the rule about
        numbers of parameter associations in a call (see 6.4).

        14.b   Ramification:  The Name Resolution Rules are the ones that
        appear under the Name Resolution Rules heading.  Some Syntax Rules
        are written in English, instead of BNF.  No rule is a Syntax Rule or
        Name Resolution Rule unless it appears under the appropriate heading.

15   {interpretation (of a constituent of a complete context)} The
interpretation of a constituent of a complete context is determined from the
overall interpretation of the complete context as a whole.  [Thus, for
example, ``interpreted as a function_call,'' means that the construct's
interpretation says that it belongs to the syntactic category function_call.]

16   {denote} [Each occurrence of] a usage name denotes the declaration
determined by its interpretation.  It also denotes the view declared by its
denoted declaration, except in the following cases:

        16.a   Ramification:  As explained below, a pragma argument is
        allowed to be ambiguous, so it can denote several declarations, and
        all of the views declared by those declarations.

   17  {current instance (of a type)} If a usage name appears within the
       declarative region of a type_declaration and denotes that same
       type_declaration, then it denotes the current instance of the
       type (rather than the type itself).  The current instance of a
       type is the object or value of the type that is associated with
       the execution that evaluates the usage name.

 17.a   Reason:  This is needed, for example, for references to the
        Access attribute from within the type_declaration.  Also, within
        a task_body or protected_body, we need to be able to denote the
        current task or protected object.  (For a single_task_
        declaration or single_protected_declaration, the rule about
        current instances is not needed.)

   18  {current instance (of a generic unit)} If a usage name appears
       within the declarative region of a generic_declaration (but not
       within its generic_formal_part) and it denotes that same generic_
       declaration, then it denotes the current instance of the generic
       unit (rather than the generic unit itself).  See also 12.3.

 18.a   To be honest:  The current instance of a generic unit is the
        instance created by whichever generic_instantiation is of
        interest at any given time.

 18.b   Ramification:  Within a generic_formal_part, a name that denotes
        the generic_declaration denotes the generic unit, which implies
        that it is not overloadable.

19   A usage name that denotes a view also denotes the entity of that view.

        19.a   Ramification:  Usually, a usage name denotes only one
        declaration, and therefore one view and one entity.

20   {expected type [distributed]} The expected type for a given expression,
name, or other construct determines, according to the type resolution rules
given below, the types considered for the construct during overload
resolution.  {type resolution rules} [The type resolution rules provide
support for class-wide programming, universal numeric literals, dispatching
operations, and anonymous access types:]

        20.a   Ramification:  Expected types are defined throughout the RM9X.
        The most important definition is that, for a subprogram, the expected
        type for the actual parameter is the type of the formal parameter.

        20.b   The type resolution rules are trivial unless either the actual
        or expected type is universal, class-wide, or of an anonymous access
        type.

   21  {type resolution rules [if any type in a specified class of types
       is expected]} {type resolution rules [if expected type is
       universal or class-wide]} If a construct is expected to be of any
       type in a class of types, or of the universal or class-wide type
       for a class, then the type of the construct shall resolve to a
       type in that class or to a universal type that covers the class.

 21.a   Ramification:  This matching rule handles (among other things)
        cases like the Val attribute, which denotes a function that
        takes a parameter of type universal_integer.

 21.b   The last part of the rule, ``or to a universal type that
        includes the class'' implies that if the expected type for an
        expression is universal_fixed, then an expression whose type is
        universal_real (such as a real literal) is OK.

   22  {type resolution rules [if expected type is specific]} If the
       expected type for a construct is a specific type T, then the type
       of the construct shall resolve either to T, or:

 22.a   Ramification:  {Beaujolais effect [partial]} This rule is not
        intended to create a preference for the specific type -- such a
        preference would cause Beaujolais effects.

          23  to T'Class; or

 23.a   Ramification:  This will only be legal as part of a call on a
        dispatching operation; see 3.9.2, ``Dispatching Operations of
        Tagged Types''.  Note that that rule is not a Name Resolution
        Rule.

          24  to a universal type that covers T; or

          25  when T is an anonymous access type (see 3.10) with
              designated type D, to an access-to-variable type whose
              designated type is D'Class or is covered by D.

 25.a   Ramification:  Because it says ``access-to-variable'' instead of
        ``access-to-object,'' two subprograms that differ only in that
        one has a parameter of an access-to-constant type, and the other
        has an access parameter, are distinguishable during overload
        resolution.

 25.b   The case where the actual is access-to-D'Class will only be
        legal as part of a call on a dispatching operation; see 3.9.2,
        ``Dispatching Operations of Tagged Types''.  Note that that rule
        is not a Name Resolution Rule.

26   {expected profile [distributed]} In certain contexts, [such as in a
subprogram_renaming_declaration,] the Name Resolution Rules define an
expected profile for a given name; {profile resolution rule (name with a
given expected profile)} in such cases, the name shall resolve to the name of
a callable entity whose profile is type conformant with the expected profile.
{type conformance (required)}

        26.a   Ramification:  The parameter and result subtypes are not used
        in overload resolution.  Only type conformance of profiles is
        considered during overload resolution.  Legality rules generally
        require at least mode-conformance in addition, but those rules are
        not used in overload resolution.


                               Legality Rules

27   {single (class expected type)} When the expected type for a construct is
required to be a single type in a given class, the type expected for the
construct shall be determinable solely from the context in which the
construct appears, excluding the construct itself, but using the requirement
that it be in the given class; the type of the construct is then this single
expected type.  Furthermore, the context shall not be one that expects any
type in some class that contains types of the given class; in particular, the
construct shall not be the operand of a type_conversion.

        27.a   Ramification:  For example, the expected type for the literal
        null is required to be a single access type.  But the expected type
        for the operand of a type_conversion is any type.  Therefore, the
        literal null is not allowed as the operand of a type_conversion.
        This is true even if there is only one access type in scope.  The
        reason for these rules is so that the compiler will not have to
        search ``everywhere'' to see if there is exactly one type in a class
        in scope.

28   A complete context shall have at least one acceptable interpretation; if
there is exactly one, then that one is chosen.

        28.a   Ramification:  This, and the rule below about ambiguity, are
        the ones that suck in all the Syntax Rules and Name Resolution Rules
        as compile-time rules.  Note that this and the ambiguity rule have to
        be Legality Rules.

29   {preference (for root numeric operators and ranges)} There is a
preference for the primitive operators (and ranges) of the root numeric types
root_integer and root_real.  In particular, if two acceptable interpretations
of a constituent of a complete context differ only in that one is for a
primitive operator (or range) of the type root_integer or root_real, and the
other is not, the interpretation using the primitive operator (or range) of
the root numeric type is preferred.

        29.a   Reason:  The reason for this preference is so that expressions
        involving literals and named numbers can be unambiguous.  For
        example, without the preference rule, the following would be
        ambiguous:

29.b        N : constant := 123;
            if N > 100 then -- Preference for root_integer "<" operator.
                ...
            end if;

30   For a complete context, if there is exactly one overall acceptable
interpretation where each constituent's interpretation is the same as or
preferred (in the above sense) over those in all other overall acceptable
interpretations, then that one overall acceptable interpretation is chosen.
{ambiguous} Otherwise, the complete context is ambiguous.

31   A complete context other than a pragma_argument_association shall not be
ambiguous.

32   A complete context that is a pragma_argument_association is allowed to
be ambiguous (unless otherwise specified for the particular pragma), but only
if every acceptable interpretation of the pragma argument is as a name that
statically denotes a callable entity.  {denote [name used as a pragma
argument]} Such a name denotes all of the declarations determined by its
interpretations, and all of the views declared by these declarations.

        32.a   Ramification:  This applies to Inline, Suppress, Import,
        Export, and Convention pragmas.  For example, it is OK to say
        ``pragma Suppress(Elaboration_Check, On => P.Q);'', even if there are
        two directly visible P's, and there are two Q's declared in the
        visible part of each P. In this case, P.Q denotes four different
        declarations.  This rule also applies to certain pragmas defined in
        the Specialized Needs Annexes.  It almost applies to Pure, Elaborate_
        Body, and Elaborate_All pragmas, but those can't have overloading for
        other reasons.

        32.b   Note that if a pragma argument denotes a call to a callable
        entity, rather than the entity itself, this exception does not apply,
        and ambiguity is disallowed.

        32.c   Note that we need to carefully define which pragma-related
        rules are Name Resolution Rules, so that, for example, a pragma
        Inline does not pick up subprograms declared in enclosing declarative
        regions, and therefore make itself illegal.

        32.d   We say ``statically denotes'' in the above rule in order to
        avoid having to worry about how many times the name is evaluated, in
        case it denotes more than one callable entity.


     NOTES
33   (16) If a usage name has only one acceptable interpretation, then it
     denotes the corresponding entity.  However, this does not mean that the
     usage name is necessarily legal since other requirements exist which are
     not considered for overload resolution; for example, the fact that an
     expression is static, whether an object is constant, mode and subtype
     conformance rules, freezing rules, order of elaboration, and so on.

     34   Similarly, subtypes are not considered for overload resolution (the
     violation of a constraint does not make a program illegal but raises an
     exception during program execution).


                        Incompatibilities With Ada 83

        34.a   {incompatibilities with Ada 83} {Beaujolais effect [partial]}
        The new preference rule for operators of root numeric types is upward
        incompatible, but only in cases that involved Beaujolais effects in
        Ada 83.  Such cases are ambiguous in Ada 9X.

                            Extensions to Ada 83

        34.b   {extensions to Ada 83} The rule that allows an expected type
        to match an actual expression of a universal type, in combination
        with the new preference rule for operators of root numeric types,
        subsumes the Ada 83 "implicit conversion" rules for universal types.

                         Wording Changes From Ada 83

        34.c   In Ada 83, it is not clear what the ``syntax rules'' are.
        AI-00157 states that a certain textual rule is a syntax rule, but
        it's still not clear how one tells in general which textual rules are
        syntax rules.  We have solved the problem by stating exactly which
        rules are syntax rules -- the ones that appear under the ``Syntax''
        heading.

        34.d   RM83 has a long list of the ``forms'' of rules that are to be
        used in overload resolution (in addition to the syntax rules).  It is
        not clear exactly which rules fall under each form.  We have solved
        the problem by explicitly marking all rules that are used in overload
        resolution.  Thus, the list of kinds of rules is unnecessary.  It is
        replaced with some introductory (intentionally vague) text explaining
        the basic idea of what sorts of rules are overloading rules.

        34.e   It is not clear from RM83 what information is embodied in a
        ``meaning'' or an ``interpretation.''  ``Meaning'' and ``inter-
        pretation'' were intended to be synonymous; we now use the latter
        only in defining the rules about overload resolution.  ``Meaning'' is
        used only informally.  This clause attempts to clarify what is meant
        by ``interpretation.''

        34.f   For example, RM83 does not make it clear that overload
        resolution is required in order to match subprogram_bodies with their
        corresponding declarations (and even to tell whether a given
        subprogram_body is the completion of a previous declaration).
        Clearly, the information needed to do this is part of the
        ``interpretation'' of a subprogram_body.  The resolution of such
        things is defined in terms of the ``expected profile'' concept.  Ada
        9X has some new cases where expected profiles are needed -- the
        resolution of P'Access, where P might denote a subprogram, is an
        example.

        34.g   RM83-8.7(2) might seem to imply that an interpretation
        embodies information about what is denoted by each usage name, but
        not information about which syntactic category each construct belongs
        to.  However, it seems necessary to include such information, since
        the Ada grammar is highly ambiguous.  For example, X(Y) might be a
        function_call or an indexed_component, and no context-free/syntactic
        information can tell the difference.  It seems like we should view
        X(Y) as being, for example, ``interpreted as a function_call'' (if
        that's what overload resolution decides it is).  Note that there are
        examples where the denotation of each usage name does not imply the
        syntactic category.  However, even if that were not true, it seems
        that intuitively, the interpretation includes that information.
        Here's an example:

34.h        type T;
            type A is access T;
            type T is array(Integer range 1..10) of A;
            I : Integer := 3;
            function F(X : Integer := 7) return A;
            Y : A := F(I); -- Ambiguous?  (We hope so.)

        34.i   Consider the declaration of Y (a complete context).  In the
        above example, overload resolution can easily determine the
        declaration, and therefore the entity, denoted by Y, A, F, and
        I. However, given all of that information, we still don't know
        whether F(I) is a function_call or an indexed_component whose prefix
        is a function_call.  (In the latter case, it is equivalent to
        F(7).all(I).)

        34.j   It seems clear that the declaration of Y ought to be
        considered ambiguous.  We describe that by saying that there are two
        interpretations, one as a function_call, and one as an indexed_
        component.  These interpretations are both acceptable to the
        overloading rules.  Therefore, the complete context is ambiguous, and
        therefore illegal.

        34.k   {Beaujolais effect [partial]} It is the intent that the Ada 9X
        preference rule for root numeric operators is more locally
        enforceable than that of RM83-4.6(15).  It should also eliminate
        interpretation shifts due to the addition or removal of a use_clause
        (the so called Beaujolais effect).

        34.l   RM83-8.7 seems to be missing some complete contexts, such as
        pragma_argument_associations, declarative_items that are not declara-
        tions or representation_clauses, and context_items.  We have added
        these, and also replaced the ``must be determinable'' wording of
        RM83-5.4(3) with the notion that the expression of a case_statement
        is a complete context.

        34.m   Cases like the Val attribute are now handled using the normal
        type resolution rules, instead of having special cases that
        explicitly allow things like ``any integer type.''



                    Section 9: Tasks and Synchronization


1   {execution [Ada program]} The execution of an Ada program consists of the
execution of one or more tasks.  {task} {interaction (between tasks)} Each
task represents a separate thread of control that proceeds independently and
concurrently between the points where it interacts with other tasks.  The
various forms of task interaction are described in this section, and include:
{parallel processing: see task} {synchronization} {concurrent processing: see
task} {intertask communication: see also task}

        1.a   To be honest:  The execution of an Ada program consists of the
        execution of one or more partitions (see 10.2), each of which in turn
        consists of the execution of an environment task and zero or more
        subtasks.

    2  the activation and termination of a task;

    3  {protected object} a call on a protected subprogram of a
       protected object, providing exclusive read-write access, or
       concurrent read-only access to shared data;

    4  a call on an entry, either of another task, allowing for
       synchronous communication with that task, or of a protected
       object, allowing for asynchronous communication with one or more
       other tasks using that same protected object;

    5  a timed operation, including a simple delay statement, a timed
       entry call or accept, or a timed asynchronous select statement
       (see next item);

    6  an asynchronous transfer of control as part of an asynchronous
       select statement, where a task stops what it is doing and begins
       execution at a different point in response to the completion of
       an entry call or the expiration of a delay;

    7  an abort statement, allowing one task to cause the termination of
       another task.

8   In addition, tasks can communicate indirectly by reading and updating
(unprotected) shared variables, presuming the access is properly synchronized
through some other kind of task interaction.


                              Static Semantics

9   {task unit} The properties of a task are defined by a corresponding task
declaration and task_body, which together define a program unit called a task
unit.


                              Dynamic Semantics

10   Over time, tasks proceed through various states.  {task state
[inactive]} {inactive (a task state)} {task state [blocked]} {blocked (a task
state)} {task state [ready]} {ready (a task state)} {task state [terminated]}
{terminated (a task state)} A task is initially inactive; upon activation,
and prior to its termination it is either blocked (as part of some task
interaction) or ready to run.  {execution resource (required for a task to
run)} While ready, a task competes for the available execution resources that
it requires to run.

        10.a   Discussion:  {task dispatching policy} {dispatching policy for
        tasks} The means for selecting which of the ready tasks to run, given
        the currently available execution resources, is determined by the
        task dispatching policy in effect, which is generally implementation
        defined, but may be controlled by pragmas and operations defined in
        the Real-Time Annex (see D.2 and D.5).


     NOTES
11   (1) Concurrent task execution may be implemented on multicomputers,
     multiprocessors, or with interleaved execution on a single physical
     processor.  On the other hand, whenever an implementation can determine
     that the required semantic effects can be achieved when parts of the
     execution of a given task are performed by different physical processors
     acting in parallel, it may choose to perform them in this way.


                         Wording Changes From Ada 83

        11.a   The introduction has been rewritten.

        11.b   We use the term "concurrent" rather than "parallel" when
        talking about logically independent execution of threads of control.
        The term "parallel" is reserved for referring to the situation where
        multiple physical processors run simultaneously.



9.1 Task Units and Task Objects

1   {task declaration} A task unit is declared by a task declaration, which
has a corresponding task_body.  A task declaration may be a task_type_
declaration, in which case it declares a named task type; alternatively, it
may be a single_task_declaration, in which case it defines an anonymous task
type, as well as declaring a named task object of that type.


                                   Syntax

2   task_type_declaration ::=
       task type defining_identifier [known_discriminant_part] [is task_definit\
ion];

3   single_task_declaration ::=
       task defining_identifier [is task_definition];

4   task_definition ::=
         {task_item}
      [ private
         {task_item}]
      end [task_identifier]

5   task_item ::= entry_declaration | representation_clause

6   task_body ::=
       task body defining_identifier is
         declarative_part
       begin
         handled_sequence_of_statements
       end [task_identifier];

    7   If a task_identifier appears at the end of a task_definition or task_
    body, it shall repeat the defining_identifier.


                               Legality Rules

8   {requires a completion [task_declaration]} A task declaration requires a
completion[, which shall be a task_body,] and every task_body shall be the
completion of some task declaration.

        8.a   To be honest:  The completion can be a pragma Import, if the
        implementation supports it.


                              Static Semantics

9   A task_definition defines a task type and its first subtype.  {visible
part [of a task unit]} The first list of task_items of a task_definition,
together with the known_discriminant_part, if any, is called the visible part
of the task unit.  {94-4426.a} {94-4873.a} {94-4881.a} [{private part [of a
task unit]} The optional list of task_items after the reserved word private
is called the private part of the task unit.]

        9.a   Proof:  Private part is defined in Section 8.


                              Dynamic Semantics

10   [{elaboration [task declaration]} The elaboration of a task declaration
elaborates the task_definition.  {elaboration [single_task_declaration]} The
elaboration of a single_task_declaration also creates an object of an
(anonymous) task type.]

        10.a   Proof:  This is redundant with the general rules for the
        elaboration of a full_type_declaration and an object_declaration.

11   {elaboration [task_definition]} [The elaboration of a task_definition
creates the task type and its first subtype;] it also includes the
elaboration of the entry_declarations in the given order.

12   {initialization [of a task object]} As part of the initialization of a
task object, any representation_clauses and any per-object constraints
associated with entry_declarations of the corresponding task_definition are
elaborated in the given order.

        12.a   Reason:  The only representation_clauses defined for task
        entries are ones that specify the Address of an entry, as part of
        defining an interrupt entry.  These clearly need to be elaborated
        per-object, not per-type.  Normally the address will be a function of
        a discriminant, if such an Address clause is in a task type rather
        than a single task declaration, though it could rely on a
        parameterless function that allocates sequential interrupt vectors.

        12.b   We do not mention representation pragmas, since each pragma
        may have its own elaboration rules.

13   {elaboration [task_body]} The elaboration of a task_body has no effect
other than to establish that tasks of the type can from then on be activated
without failing the Elaboration_Check.

14   [The execution of a task_body is invoked by the activation of a task of
the corresponding type (see 9.2).]

15   The content of a task object of a given task type includes:

   16  The values of the discriminants of the task object, if any;

   17  An entry queue for each entry of the task object;

 17.a   Ramification:  "For each entry" implies one queue for each
        single entry, plus one for each entry of each entry family.

   18  A representation of the state of the associated task.


     NOTES
19   (2) Within the declaration or body of a task unit, the name of the task
     unit denotes the current instance of the unit (see 8.6), rather than the
     first subtype of the corresponding task type (and thus the name cannot
     be used as a subtype_mark).

   19.a   Discussion:  However, it is possible to refer to some other subtype
        of the task type within its body, presuming such a subtype has been
        declared between the task_type_declaration and the task_body.

20   (3) The notation of a selected_component can be used to denote a
     discriminant of a task (see 4.1.3).  Within a task unit, the name of a
     discriminant of the task type denotes the corresponding discriminant of
     the current instance of the unit.

21   (4) A task type is a limited type (see 7.5), and hence has neither an
     assignment operation nor predefined equality operators.  If an
     application needs to store and exchange task identities, it can do so by
     defining an access type designating the corresponding task objects and
     by using access values for identification purposes.  Assignment is
     available for such an access type as for any access type.
     Alternatively, if the implementation supports the Systems Programming
     Annex, the Identity attribute can be used for task identification (see
     C.7).
                                  Examples

22   Examples of declarations of task types:

23  task type Server is
       entry Next_Work_Item(WI : in Work_Item);
       entry Shut_Down;
    end Server;

24  task type Keyboard_Driver(ID : Keyboard_ID := New_ID) is
       entry Read (C : out Character);
       entry Write(C : in  Character);
    end Keyboard_Driver;

25   Examples of declarations of single tasks:

26  task Controller is
       entry Request(Level)(D : Item);  --  a family of entries
    end Controller;

27  task Parser is
       entry Next_Lexeme(L : in  Lexical_Element);
       entry Next_Action(A : out Parser_Action);
    end;

28  task User;  --  has no entries

29   Examples of task objects:

30  Agent    : Server;
    Teletype : Keyboard_Driver(TTY_ID);
    Pool     : array(1 .. 10) of Keyboard_Driver;

31   Example of access type designating task objects:

32  type Keyboard is access Keyboard_Driver;
    Terminal : Keyboard := new Keyboard_Driver(Term_ID);


                            Extensions to Ada 83

        32.a   {extensions to Ada 83} The syntax rules for task declarations
        are modified to allow a known_discriminant_part, and to allow a
        private part.  They are also modified to allow entry_declarations and
        representation_clauses to be mixed.

                         Wording Changes From Ada 83

        32.b   The syntax rules for tasks have been split up according to
        task types and single tasks.  In particular:  The syntax rules for
        task_declaration and task_specification are removed.  The syntax
        rules for task_type_declaration, single_task_declaration, task_
        definition and task_item are new.

        32.c   The syntax rule for task_body now uses the nonterminal
        handled_sequence_of_statements.

        32.d   The declarative_part of a task_body is now required; that
        doesn't make any real difference, because a declarative_part can be
        empty.



9.2 Task Execution - Task Activation

                              Dynamic Semantics

1   {execution [task]} The execution of a task of a given task type consists
of the execution of the corresponding task_body.  {execution [task_body]}
{task (execution)} {activation (of a task)} {task (activation)} The initial
part of this execution is called the activation of the task; it consists of
the elaboration of the declarative_part of the task_body.  {activation
failure} Should an exception be propagated by the elaboration of its
declarative_part, the activation of the task is defined to have failed, and
it becomes a completed task.

2   A task object (which represents one task) can be created either as part
of the elaboration of an object_declaration occurring immediately within some
declarative region, or as part of the evaluation of an allocator.  All tasks
created by the elaboration of object_declarations of a single declarative
region (including subcomponents of the declared objects) are activated
together.  Similarly, all tasks created by the evaluation of a single
allocator are activated together.  The activation of a task is associated
with the innermost allocator or object_declaration that is responsible for
its creation.

        2.a   Discussion:  The initialization of an object_declaration or
        allocator can indirectly include the creation of other objects that
        contain tasks.  For example, the default expression for a
        subcomponent of an object created by an allocator might call a
        function that evaluates a completely different allocator.  Tasks
        created by the two allocators are not activated together.

3   For tasks created by the elaboration of object_declarations of a given
declarative region, the activations are initiated within the context of the
handled_sequence_of_statements (and its associated exception_handlers if any
-- see 11.2), just prior to executing the statements of the _sequence.  [For
a package without an explicit body or an explicit handled_sequence_of_
statements, an implicit body or an implicit null_statement is assumed, as
defined in 7.2.]

        3.a   Ramification:  If Tasking_Error is raised, it can be handled by
        handlers of the handled_sequence_of_statements.

4   For tasks created by the evaluation of an allocator, the activations are
initiated as the last step of evaluating the allocator, after completing any
initialization for the object created by the allocator, and prior to
returning the new access value.

5   {activator (of a task)} {blocked [waiting for activations to complete]}
The task that created the new tasks and initiated their activations (the
activator) is blocked until all of these activations complete (successfully
or not).  {Tasking_Error (raised by failure of run-time check)} Once all of
these activations are complete, if the activation of any of the tasks has
failed [(due to the propagation of an exception)], Tasking_Error is raised in
the activator, at the place at which it initiated the activations.
Otherwise, the activator proceeds with its execution normally.  Any tasks
that are aborted prior to completing their activation are ignored when
determining whether to raise Tasking_Error.

        5.a   Ramification:  Note that a task created by an allocator does
        not necessarily depend on its activator; in such a case the
        activator's termination can precede the termination of the newly
        created task.

        5.b   Discussion:  Tasking_Error is raised only once, even if two or
        more of the tasks being activated fail their activation.

6   Should the task that created the new tasks never reach the point where it
would initiate the activations (due to an abort or the raising of an
exception), the newly created tasks become terminated and are never
activated.


     NOTES
7    (5) An entry of a task can be called before the task has been activated.

8    (6) If several tasks are activated together, the execution of any of
     these tasks need not await the end of the activation of the other tasks.

9    (7) A task can become completed during its activation either because of
     an exception or because it is aborted (see 9.8).


                                  Examples

10   Example of task activation:

11  procedure P is
       A, B : Server;    --  elaborate the task objects A, B
       C    : Server;    --  elaborate the task object C
    begin
       --  the tasks A, B, C are activated together before the first statement
       ...
    end;


                         Wording Changes From Ada 83

        11.a   We have replaced the term suspended with blocked, since we
        didn't want to consider a task blocked when it was simply competing
        for execution resources.  "Suspended" is sometimes used more
        generally to refer to tasks that are not actually running on some
        processor, due to the lack of resources.

        11.b   This clause has been rewritten in an attempt to improve
        presentation.



9.3 Task Dependence - Termination of Tasks

                              Dynamic Semantics

1   {dependence (of a task on a master)} {task (dependence)} {task
(completion)} {task (termination)} Each task (other than an environment task
-- see 10.2) depends on one or more masters (see 7.6.1), as follows:

    2  If the task is created by the evaluation of an allocator for a
       given access type, it depends on each master that includes the
       elaboration of the declaration of the ultimate ancestor of the
       given access type.

    3  If the task is created by the elaboration of an object_
       declaration, it depends on each master that includes this
       elaboration.  {94-4715.a}

4   {dependence (of a task on another task)} Furthermore, if a task depends
on a given master, it is defined to depend on the task that executes the
master, and (recursively) on any master of that task.

        4.a   Discussion:  Don't confuse these kinds of dependences with the
        dependences among compilation units defined in 10.1.1, ``Compilation
        Units - Library Units''.

5   A task is said to be completed when the execution of its corresponding
task_body is completed.  A task is said to be terminated when any
finalization of the task_body has been performed (see 7.6.1).  [The first
step of finalizing a master (including a task_body) is to wait for the
termination of any tasks dependent on the master.]  {blocked [waiting for
dependents to terminate]} The task executing the master is blocked until all
the dependents have terminated.  [Any remaining finalization is then
performed and the master is left.]

6   Completion of a task (and the corresponding task_body) can occur when the
task is blocked at a select_statement with an an open terminate_alternative
(see 9.7.1); the open terminate_alternative is selected if and only if the
following conditions are satisfied:

    7  The task depends on some completed master; {94-4715.a}

    8  Each task that depends on the master considered is either already
       terminated or similarly blocked at a select_statement with an
       open terminate_alternative.

9   When both conditions are satisfied, the task considered becomes
completed, together with all tasks that depend on the master considered that
are not yet completed.

        9.a   Ramification:  Any required finalization is performed after the
        selection of terminate_alternatives.  The tasks are not callable
        during the finalization.  In some ways it is as though they were
        aborted.


     NOTES
10   (8) The full view of a limited private type can be a task type, or can
     have subcomponents of a task type.  Creation of an object of such a type
     creates dependences according to the full type.

11   (9) An object_renaming_declaration defines a new view of an existing
     entity and hence creates no further dependence.

12   (10) The rules given for the collective completion of a group of tasks
     all blocked on select_statements with open terminate_alternatives ensure
     that the collective completion can occur only when there are no
     remaining active tasks that could call one of the tasks being
     collectively completed.

13   (11) If two or more tasks are blocked on select_statements with open
     terminate_alternatives, and become completed collectively, their
     finalization actions proceed concurrently.

14   (12) The completion of a task can occur due to any of the following:

        15  the raising of an exception during the elaboration of the
            declarative_part of the corresponding task_body;

        16  the completion of the handled_sequence_of_statements of the
            corresponding task_body;

        17  the selection of an open terminate_alternative of a select_
            statement in the corresponding task_body;

        18  the abort of the task.


                                  Examples

19   Example of task dependence:

20  declare
       type Global is access Server;        --  see 9.1
       A, B : Server;
       G    : Global;
    begin
       --  activation of A and B
       declare
          type Local is access Server;
          X : Global := new Server;  --  activation of X.all
          L : Local  := new Server;  --  activation of L.all
          C : Server;
       begin
          --  activation of C
          G := X;  --  both G and X designate the same task object
          ...
       end;  --  await termination of C and L.all (but not X.all)
       ...
    end;  --  await termination of A, B, and G.all


                         Wording Changes From Ada 83

        20.a   We have revised the wording to be consistent with the
        definition of master now given in 7.6.1, ``Completion and
        Finalization''.

        20.b   Tasks that used to depend on library packages in Ada 83, now
        depend on the (implicit) task_body of the environment task (see
        10.2).  Therefore, the environment task has to wait for them before
        performing library level finalization and terminating the partition.
        In Ada 83 the requirement to wait for tasks that depended on library
        packages was not as clear.

        20.c   What was "collective termination" is now "collective
        completion" resulting from selecting terminate_alternatives.  This is
        because finalization still occurs for such tasks, and this happens
        after selecting the terminate_alternative, but before termination.



9.4 Protected Units and Protected Objects

1   {protected object} {protected operation} {protected subprogram}
{protected entry} A protected object provides coordinated access to shared
data, through calls on its visible protected operations, which can be
protected subprograms or protected entries.  {protected declaration}
{protected unit} {protected declaration} A protected unit is declared by a
protected declaration, which has a corresponding protected_body.  A protected
declaration may be a protected_type_declaration, in which case it declares a
named protected type; alternatively, it may be a single_protected_
declaration, in which case it defines an anonymous protected type, as well as
declaring a named protected object of that type.  {broadcast signal: see
protected object}


                                   Syntax

2   protected_type_declaration ::=
      protected type defining_identifier [known_discriminant_part] is protected\
_definition;

3   single_protected_declaration ::=
      protected defining_identifier is protected_definition;

4   protected_definition ::=
        { protected_operation_declaration }
    [ private
        { protected_element_declaration } ]
      end [protected_identifier]

5   protected_operation_declaration ::= subprogram_declaration
         | entry_declaration
         | representation_clause

6   protected_element_declaration ::= protected_operation_declaration
         | component_declaration

        6.a   Reason:  We allow the operations and components to be mixed
        because that's how other things work (for example, package
        declarations).  We have relaxed the ordering rules for the items
        inside declarative_parts and task_definitions as well.

7   protected_body ::=
      protected body defining_identifier is
       { protected_operation_item }
      end [protected_identifier];

8   protected_operation_item ::= subprogram_declaration
         | subprogram_body
         | entry_body
         | representation_clause

    9   If a protected_identifier appears at the end of a protected_
    definition or protected_body, it shall repeat the defining_identifier.


                               Legality Rules

10   {requires a completion [protected_declaration]} A protected declaration
requires a completion[, which shall be a protected_body,] and every
protected_body shall be the completion of some protected declaration.

        10.a   To be honest:  The completion can be a pragma Import, if the
        implementation supports it.


                              Static Semantics

11   A protected_definition defines a protected type and its first subtype.
{visible part [of a protected unit]} The list of protected_operation_
declarations of a protected_definition, together with the known_discriminant_
part, if any, is called the visible part of the protected unit.  {94-4426.a}
{94-4873.a} {94-4881.a} [{private part [of a protected unit]} The optional
list of protected_element_declarations after the reserved word private is
called the private part of the protected unit.]

        11.a   Proof:  Private part is defined in Section 8.


                              Dynamic Semantics

12   [{elaboration [protected declaration]} The elaboration of a protected
declaration elaborates the protected_definition.  {elaboration [single_
protected_declaration]} The elaboration of a single_protected_declaration
also creates an object of an (anonymous) protected type.]

        12.a   Proof:  This is redundant with the general rules for the
        elaboration of a full_type_declaration and an object_declaration.

13   {elaboration [protected_definition]} [The elaboration of a protected_
definition creates the protected type and its first subtype;] it also
includes the elaboration of the component_declarations and protected_
operation_declarations in the given order.

14   [{initialization [of a protected object]} As part of the initialization
of a protected object, any per-object constraints (see 3.8) are elaborated.]

        14.a   Discussion:  We do not mention pragmas since each pragma has
        its own elaboration rules.

15   {elaboration [protected_body]} The elaboration of a protected_body has
no other effect than to establish that protected operations of the type can
from then on be called without failing the Elaboration_Check.

16   The content of an object of a given protected type includes:

   17  The values of the components of the protected object, including
       (implicitly) an entry queue for each entry declared for the
       protected object;

 17.a   Ramification:  "For each entry" implies one queue for each
        single entry, plus one for each entry of each entry family.

   18  {execution resource [associated with a protected object]} A
       representation of the state of the execution resource associated
       with the protected object (one such resource is associated with
       each protected object).

19   [The execution resource associated with a protected object has to be
acquired to read or update any components of the protected object; it can be
acquired (as part of a protected action -- see 9.5.1) either for concurrent
read-only access, or for exclusive read-write access.]

20   {finalization [of a protected object]} {Program_Error (raised by failure
of run-time check)} As the first step of the finalization of a protected
object, each call remaining on any entry queue of the object is removed from
its queue and Program_Error is raised at the place of the corresponding
entry_call_statement.

        20.a   Reason:  This is analogous to the raising of Tasking_Error in
        callers of a task that completes before accepting the calls.  This
        situation can only occur due to a requeue (ignoring premature
        unchecked_deallocation), since any task that has accessibility to a
        protected object is awaited before finalizing the protected object.
        For example:

20.b        procedure Main is
                task T is
                    entry E;
                end T;

20.c            task body T is
                    protected PO is
                        entry Ee;
                    end PO;

20.d                protected body PO is
                        entry Ee when False is
                        begin
                            null;
                        end Ee;
                    end PO;
                begin
                    accept E do
                        requeue PO.Ee;
                    end E;
                end T;
            begin
                T.E;
            end Main;

        20.e   The environment task is queued on PO.EE when PO is finalized.

        20.f   In a real example, a server task might park callers on a local
        protected object for some useful purpose, so we didn't want to
        disallow this case.


     NOTES
21   (13) Within the declaration or body of a protected unit, the name of the
     protected unit denotes the current instance of the unit (see 8.6),
     rather than the first subtype of the corresponding protected type (and
     thus the name cannot be used as a subtype_mark).

   21.a   Discussion:  However, it is possible to refer to some other subtype
        of the protected type within its body, presuming such a subtype has
        been declared between the protected_type_declaration and the
        protected_body.

22   (14) A selected_component can be used to denote a discriminant of a
     protected object (see 4.1.3).  Within a protected unit, the name of a
     discriminant of the protected type denotes the corresponding
     discriminant of the current instance of the unit.

23   (15) A protected type is a limited type (see 7.5), and hence has neither
     an assignment operation nor predefined equality operators.

24   (16) The bodies of the protected operations given in the protected_body
     define the actions that take place upon calls to the protected
     operations.

25   (17) The declarations in the private part are only visible within the
     private part and the body of the protected unit.

   25.a   Reason:  Component_declarations are disallowed in a protected_body
        because, for efficiency, we wish to allow the compiler to determine
        the size of protected objects (when not dynamic); the compiler cannot
        necessarily see the body.  Furthermore, the semantics of
        initialization of such objects would be problematic -- we do not wish
        to give protected objects complex initialization semantics similar to
        task activation.

   25.b   The same applies to entry_declarations, since an entry involves an
        implicit component -- the entry queue.


                                  Examples

26   Example of declaration of protected type and corresponding body:

27  protected type Resource is
       entry Seize;
       procedure Release;
    private
       Busy : Boolean := False;
    end Resource;

28  protected body Resource is
       entry Seize when not Busy is
       begin
          Busy := True;
       end Seize;

29     procedure Release is
       begin
          Busy := False;
       end Release;
    end Resource;

30   Example of a single protected declaration and corresponding body:

31  protected Shared_Array is
       --  Index, Item, and Item_Array are global types
       function  Component    (N : in Index) return Item;
       procedure Set_Component(N : in Index; E : in  Item);
    private
       Table : Item_Array(Index) := (others => Null_Item);
    end Shared_Array;

32  protected body Shared_Array is
       function Component(N : in Index) return Item is
       begin
          return Table(N);
       end Component;

33     procedure Set_Component(N : in Index; E : in Item) is
       begin
          Table(N) := E;
       end Set_Component;
    end Shared_Array;

34   Examples of protected objects:

35  Control  : Resource;
    Flags    : array(1 .. 100) of Resource;


                            Extensions to Ada 83

        35.a   {extensions to Ada 83} This entire clause is new; protected
        units do not exist in Ada 83.



9.5 Intertask Communication

1   {intertask communication} {critical section: see intertask communication}
The primary means for intertask communication is provided by calls on entries
and protected subprograms.  Calls on protected subprograms allow coordinated
access to shared data objects.  Entry calls allow for blocking the caller
until a given condition is satisfied (namely, that the corresponding entry is
open -- see 9.5.3), and then communicating data or control information
directly with another task or indirectly via a shared protected object.


                              Static Semantics

2   {target object (of a call on an entry or a protected subprogram)} Any
call on an entry or on a protected subprogram identifies a target object for
the operation, which is either a task (for an entry call) or a protected
object (for an entry call or a protected subprogram call).  The target object
is considered an implicit parameter to the operation, and is determined by
the operation name (or prefix) used in the call on the operation, as follows:

    3  If it is a direct_name or expanded name that denotes the
       declaration (or body) of the operation, then the target object is
       implicitly specified to be the current instance of the task or
       protected unit immediately enclosing the operation; {internal
       call} such a call is defined to be an internal call;

    4  If it is a selected_component that is not an expanded name, then
       the target object is explicitly specified to be the task or
       protected object denoted by the prefix of the name; {external
       call} such a call is defined to be an external call;

 4.a    Discussion:  For example:

4.b         protected type Pt is
              procedure Op1;
              procedure Op2;
            end Pt;

4.c         PO : Pt;
            Other_Object : Some_Other_Protected_Type;

4.d         protected body Pt is
              procedure Op1 is begin ... end Op1;

4.e           procedure Op2 is
              begin
                Op1; -- An internal call.
                Pt.Op1; -- Another internal call.
                PO.Op1; -- An external call.  It the current instance is PO, th\
en
                        -- this is a bounded error (see 9.5.1).
                Other_Object.Some_Op; -- An external call.
              end Op2;
            end Pt;

    5  If the name or prefix is a dereference (implicit or explicit) of
       an access-to-protected-subprogram value, then the target object
       is determined by the prefix of the Access attribute_reference
       that produced the access value originally, and the call is
       defined to be an external call;

    6  If the name or prefix denotes a subprogram_renaming_declaration,
       then the target object is as determined by the name of the
       renamed entity.

7   {target object (of a requeue_statement)} {internal requeue} {external
requeue} A corresponding definition of target object applies to a requeue_
statement (see 9.5.4), with a corresponding distinction between an internal
requeue and an external requeue.


                              Dynamic Semantics

8   Within the body of a protected operation, the current instance (see 8.6)
of the immediately enclosing protected unit is determined by the target
object specified (implicitly or explicitly) in the call (or requeue) on the
protected operation.

        8.a   To be honest:  The current instance is defined in the same way
        within the body of a subprogram declared immediately within a
        protected_body.

9   Any call on a protected procedure or entry of a target protected object
is defined to be an update to the object, as is a requeue on such an entry.

        9.a   Reason:  Read/write access to the components of a protected
        object is granted while inside the body of a protected procedure or
        entry.  Also, any protected entry call can change the value of the
        Count attribute, which represents an update.  Any protected procedure
        call can result in servicing the entries, which again might change
        the value of a Count attribute.



9.5.1 Protected Subprograms and Protected Actions

1   {protected subprogram} {protected procedure} {protected function} A
protected subprogram is a subprogram declared immediately within a protected_
definition.  Protected procedures provide exclusive read-write access to the
data of a protected object; protected functions provide concurrent read-only
access to the data.

        1.a   Ramification:  A subprogram declared immediately within a
        protected_body is not a protected subprogram; it is an intrinsic
        subprogram.  See 6.3.1, ``Conformance Rules''.


                              Static Semantics

2   Within the body of a protected function (or a function declared
immediately within a protected_body), the current instance of the enclosing
protected unit is defined to be a constant [(that is, its subcomponents may
be read but not updated)].  Within the body of a protected procedure (or a
procedure declared immediately within a protected_body), and within an entry_
body, the current instance is defined to be a variable [(updating is
permitted)].

        2.a   Ramification:  The current instance is like an implicit
        parameter, of mode in for a protected function, and of mode in out
        for a protected procedure (or protected entry).


                              Dynamic Semantics

3   {execution [protected subprogram call]} For the execution of a call on a
protected subprogram, the evaluation of the name or prefix and of the
parameter associations, and any assigning back of in out or out parameters,
proceeds as for a normal subprogram call (see 6.4).  If the call is an
internal call (see 9.5), the body of the subprogram is executed as for a
normal subprogram call.  If the call is an external call, then the body of
the subprogram is executed as part of a new protected action on the target
protected object; the protected action completes after the body of the
subprogram is executed.  [A protected action can also be started by an entry
call (see 9.5.3).]

4   {protected action} A new protected action is not started on a protected
object while another protected action on the same protected object is
underway, unless both actions are the result of a call on a protected
function.  This rule is expressible in terms of the execution resource
associated with the protected object:

    5  {protected action (start)} {acquire (execution resource
       associated with protected object)} Starting a protected action on
       a protected object corresponds to acquiring the execution
       resource associated with the protected object, either for
       concurrent read-only access if the protected action is for a call
       on a protected function, or for exclusive read-write access
       otherwise;

    6  {protected action (complete)} {release (execution resource
       associated with protected object)} Completing the protected
       action corresponds to releasing the associated execution
       resource.

7   [After performing an operation on a protected object other than a call on
a protected function, but prior to completing the associated protected
action, the entry queues (if any) of the protected object are serviced (see
9.5.3).]


                          Bounded (Run-Time) Errors

8   {bounded error} During a protected action, it is a bounded error to
invoke an operation that is potentially blocking.  {potentially blocking
operation} {blocking, potentially} The following are defined to be
potentially blocking operations:

        8.a   Reason:  Some of these operations are not directly blocking.
        However, they are still treated as bounded errors during a protected
        action, because allowing them might impose an undesirable
        implementation burden.

    9  a select_statement;

   10  an accept_statement;

   11  an entry_call_statement;

   12  a delay_statement;

   13  an abort_statement;

   14  task creation or activation;

   15  an external call on a protected subprogram (or an external
       requeue) with the same target object as that of the protected
       action;

 15.a   Reason:  This is really a deadlocking call, rather than a
        blocking call, but we include it in this list for simplicity.

   16  a call on a subprogram whose body contains a potentially blocking
       operation.

 16.a   Reason:  This allows an implementation to check and raise
        Program_Error as soon as a subprogram is called, rather than
        waiting to find out whether it actually reaches the potentially
        blocking operation.  This in turn allows the potentially
        blocking operation check to be performed prior to run time in
        some environments.

17   {Program_Error (raised by failure of run-time check)} If the bounded
error is detected, Program_Error is raised.  If not detected, the bounded
error might result in deadlock or a (nested) protected action on the same
target object.

18   Certain language-defined subprograms are potentially blocking.  In
particular, the subprograms of the language-defined input-output packages
that manipulate files (implicitly or explicitly) are potentially blocking.
Other potentially blocking subprograms are identified where they are defined.
When not specified as potentially blocking, a language-defined subprogram is
nonblocking.


     NOTES
19   (18) If two tasks both try to start a protected action on a protected
     object, and at most one is calling a protected function, then only one
     of the tasks can proceed.  Although the other task cannot proceed, it is
     not considered blocked, and it might be consuming processing resources
     while it awaits its turn.  There is no language-defined ordering or
     queuing presumed for tasks competing to start a protected action -- on a
     multiprocessor such tasks might use busy-waiting; for monoprocessor
     considerations, see D.3, ``Priority Ceiling Locking''.

   19.a   Discussion:  The intended implementation on a multi-processor is in
        terms of ``spin locks'' -- the waiting task will spin.

20   (19) The body of a protected unit may contain declarations and bodies
     for local subprograms.  These are not visible outside the protected
     unit.

21   (20) The body of a protected function can contain internal calls on
     other protected functions, but not protected procedures, because the
     current instance is a constant.  On the other hand, the body of a
     protected procedure can contain internal calls on both protected
     functions and procedures.

22   (21) From within a protected action, an internal call on a protected
     subprogram, or an external call on a protected subprogram with a
     different target object is not considered a potentially blocking
     operation.

   22.a   Reason:  This is because a task is not considered blocked while
        attempting to acquire the execution resource associated with a
        protected object.  The acquisition of such a resource is rather
        considered part of the normal competition for execution resources
        between the various tasks that are ready.  External calls that turn
        out to be on the same target object are considered potentially
        blocking, since they can deadlock the task indefinitely.


                                  Examples

23   Examples of protected subprogram calls (see 9.4):

24  Shared_Array.Set_Component(N, E);
    E := Shared_Array.Component(M);
    Control.Release;



9.5.2 Entries and Accept Statements

1   Entry_declarations, with the corresponding entry_bodies or accept_
statements, are used to define potentially queued operations on tasks and
protected objects.


                                   Syntax

2   entry_declaration ::=
       entry defining_identifier [(discrete_subtype_definition)] parameter_prof\
ile;

3   accept_statement ::=
       accept entry_direct_name [(entry_index)] parameter_profile [do
         handled_sequence_of_statements
       end [entry_identifier]];

        3.a   Reason:  We cannot use defining_identifier for accept_
        statements.  Although an accept_statement is sort of like a body, it
        can appear nested within a block_statement, and therefore be hidden
        from its own entry by an outer homograph.

4   entry_index ::= expression

5   entry_body ::=
      entry defining_identifier  entry_body_formal_part  entry_barrier is
        declarative_part
      begin
        handled_sequence_of_statements
      end [entry_identifier];

6   entry_body_formal_part ::= [(entry_index_specification)] parameter_profile

7   entry_barrier ::= when condition

8   entry_index_specification ::= for defining_identifier in discrete_subtype_d\
efinition

    9   If an entry_identifier appears at the end of an accept_statement, it
    shall repeat the entry_direct_name.  If an entry_identifier appears at
    the end of an entry_body, it shall repeat the defining_identifier.

    10   [An entry_declaration is allowed only in a protected or task
    declaration.]

        10.a   Proof:  This follows from the BNF.


                            Name Resolution Rules

11   {expected profile [accept_statement entry_direct_name]} In an accept_
statement, the expected profile for the entry_direct_name is that of the
entry_declaration; {expected type [entry_index]} the expected type for an
entry_index is that of the subtype defined by the discrete_subtype_definition
of the corresponding entry_declaration.

12   Within the handled_sequence_of_statements of an accept_statement, if a
selected_component has a prefix that denotes the corresponding entry_
declaration, then the entity denoted by the prefix is the accept_statement,
and the selected_component is interpreted as an expanded name (see 4.1.3)[;
the selector_name of the selected_component has to be the identifier for some
formal parameter of the accept_statement].

        12.a   Proof:  The only declarations that occur immediately within
        the declarative region of an accept_statement are those for its
        formal parameters.


                               Legality Rules

13   An entry_declaration in a task declaration shall not contain a
specification for an access parameter (see 3.10).

        13.a   Reason:  Access parameters for task entries would require a
        complex implementation.  For example:

13.b        task T is
               entry E(Z : access Integer); -- Illegal!
            end T;

13.c        task body T is
            begin
               declare
                  type A is access all Integer;
                  X : A;
                  Int : aliased Integer;
                  task Inner;
                  task body Inner is
                  begin
                     T.E(Int'Access);
                  end Inner;
               begin
                  accept E(Z : access Integer) do
                     X := A(Z); -- Accessibility_Check
                  end E;
               end;
            end T;

        13.d   Implementing the Accessibility_Check inside the accept_
        statement for E is difficult, since one does not know whether the
        entry caller is calling from inside the immediately enclosing declare
        block or from outside it.  This means that the lexical nesting level
        associated with the designated object is not sufficient to determine
        whether the Accessibility_Check should pass or fail.

        13.e   Note that such problems do not arise with protected entries,
        because entry_bodies are always nested immediately within the
        protected_body; they cannot be further nested as can accept_
        statements, nor can they be called from within the protected_body
        (since no entry calls are permitted inside a protected_body).

14   For an accept_statement, the innermost enclosing body shall be a task_
body, and the entry_direct_name shall denote an entry_declaration in the
corresponding task declaration; the profile of the accept_statement shall
conform fully to that of the corresponding entry_declaration.  {full
conformance (required)} An accept_statement shall have a parenthesized entry_
index if and only if the corresponding entry_declaration has a discrete_
subtype_definition.

15   An accept_statement shall not be within another accept_statement that
corresponds to the same entry_declaration, nor within an asynchronous_select
inner to the enclosing task_body.

        15.a   Reason:  Accept_statements are required to be immediately
        within the enclosing task_body (as opposed to being in a nested
        subprogram) to ensure that a nested task does not attempt to accept
        the entry of its enclosing task.  We considered relaxing this
        restriction, either by making the check a run-time check, or by
        allowing a nested task to accept an entry of its enclosing task.
        However, neither change seemed to provide sufficient benefit to
        justify the additional implementation burden.

        15.b   Nested accept_statements for the same entry (or entry family)
        are prohibited to ensure that there is no ambiguity in the resolution
        of an expanded name for a formal parameter of the entry.  This could
        be relaxed by allowing the inner one to hide the outer one from all
        visibility, but again the small added benefit didn't seem to justify
        making the change for Ada 9X.

        15.c   Accept_statements are not permitted within asynchronous_select
        statements to simplify the semantics and implementation:  an accept_
        statement in an abortable_part could result in Tasking_Error being
        propagated from an entry call even though the target task was still
        callable; implementations that use multiple tasks implicitly to
        implement an asynchronous_select might have trouble supporting
        "up-level" accepts.  Furthermore, if accept_statements were permitted
        in the abortable_part, a task could call its own entry and then
        accept it in the abortable_part, leading to rather unusual and
        possibly difficult-to-specify semantics.

16   {requires a completion [protected entry_declaration]} An entry_
declaration of a protected unit requires a completion[, which shall be an
entry_body,] {only as a completion [entry_body]} and every entry_body shall
be the completion of an entry_declaration of a protected unit.  {completion
legality [entry_body]} The profile of the entry_body shall conform fully to
that of the corresponding declaration.  {full conformance (required)}

        16.a   Ramification:  An entry_declaration, unlike a subprogram_
        declaration, cannot be completed with a renaming_declaration.

        16.b   To be honest:  The completion can be a pragma Import, if the
        implementation supports it.

        16.c   Discussion:  The above applies only to protected entries,
        which are the only ones completed with entry_bodies.  Task entries
        have corresponding accept_statements instead of having entry_bodies,
        and we do not consider an accept_statement to be a ``completion,''
        because a task entry_declaration is allowed to have zero, one, or
        more than one corresponding accept_statements.

17   An entry_body_formal_part shall have an entry_index_specification if and
only if the corresponding entry_declaration has a discrete_subtype_
definition.  In this case, the discrete_subtype_definitions of the entry_
declaration and the entry_index_specification shall fully conform to one
another (see 6.3.1).  {full conformance (required)}

18   A name that denotes a formal parameter of an entry_body is not allowed
within the entry_barrier of the entry_body.


                              Static Semantics

19   The parameter modes defined for parameters in the parameter_profile of
an entry_declaration are the same as for a subprogram_declaration and have
the same meaning (see 6.2).

        19.a   Discussion:  Note that access parameters are not allowed for
        task entries (see above).

20   {family (entry)} {entry family} {entry index subtype} An entry_
declaration with a discrete_subtype_definition (see 3.6) declares a family of
distinct entries having the same profile, with one such entry for each value
of the entry index subtype defined by the discrete_subtype_definition.  [A
name for an entry of a family takes the form of an indexed_component, where
the prefix denotes the entry_declaration for the family, and the index value
identifies the entry within the family.]  {single entry} {entry (single)} The
term single entry is used to refer to any entry other than an entry of an
entry family.

21   In the entry_body for an entry family, the entry_index_specification
declares a named constant whose subtype is the entry index subtype defined by
the corresponding entry_declaration; {named entry index} the value of the
named entry index identifies which entry of the family was called.

        21.a   Ramification:  The discrete_subtype_definition of the entry_
        index_specification is not elaborated; the subtype of the named
        constant declared is defined by the discrete_subtype_definition of
        the corresponding entry_declaration, which is elaborated, either when
        the type is declared, or when the object is created, if its
        constraint is per-object.


                              Dynamic Semantics

22   {elaboration [entry_declaration]} For the elaboration of an entry_
declaration for an entry family, if the discrete_subtype_definition contains
no per-object expressions (see 3.8), then the discrete_subtype_definition is
elaborated.  Otherwise, the elaboration of the entry_declaration consists of
the evaluation of any expression of the discrete_subtype_definition that is
not a per-object expression (or part of one).  The elaboration of an entry_
declaration for a single entry has no effect.

        22.a   Discussion:  The elaboration of the declaration of a protected
        subprogram has no effect, as specified in clause 6.1.  The default
        initialization of an object of a task or protected type is covered in
        3.3.1.

23   [The actions to be performed when an entry is called are specified by
the corresponding accept_statements (if any) for an entry of a task unit, and
by the corresponding entry_body for an entry of a protected unit.]

24   {execution [accept_statement]} For the execution of an accept_statement,
the entry_index, if any, is first evaluated and converted to the entry index
subtype; this index value identifies which entry of the family is to be
accepted.  {implicit subtype conversion [entry index]} {blocked [on an
accept_statement]} {selection (of an entry caller)} Further execution of the
accept_statement is then blocked until a caller of the corresponding entry is
selected (see 9.5.3), whereupon the handled_sequence_of_statements, if any,
of the accept_statement is executed, with the formal parameters associated
with the corresponding actual parameters of the selected entry call.  Upon
completion of the handled_sequence_of_statements, the accept_statement
completes and is left.  When an exception is propagated from the handled_
sequence_of_statements of an accept_statement, the same exception is also
raised by the execution of the corresponding entry_call_statement.

        24.a   Ramification:  This is in addition to propagating it to the
        construct containing the accept_statement.  In other words, for a
        rendezvous, the raising splits in two, and continues concurrently in
        both tasks.

        24.b   The caller gets a new occurrence; this isn't considered
        propagation.

        24.c   Note that we say ``propagated from the handled_sequence_of_
        statements of an accept_statement'', not ``propagated from an accept_
        statement.''  The latter would be wrong -- we don't want exceptions
        propagated by the entry_index to be sent to the caller (there is none
        yet!).

25   {rendezvous} The above interaction between a calling task and an
accepting task is called a rendezvous.  [After a rendezvous, the two tasks
continue their execution independently.]

26   [An entry_body is executed when the condition of the entry_barrier
evaluates to True and a caller of the corresponding single entry, or entry of
the corresponding entry family, has been selected (see 9.5.3).]  {execution
[entry_body]} For the execution of the entry_body, the declarative_part of
the entry_body is elaborated, and the handled_sequence_of_statements of the
body is executed, as for the execution of a subprogram_body.  The value of
the named entry index, if any, is determined by the value of the entry index
specified in the entry_name of the selected entry call (or intermediate
requeue_statement -- see 9.5.4).

        26.a   To be honest:  If the entry had been renamed as a subprogram,
        and the call was a procedure_call_statement using the name declared
        by the renaming, the entry index (if any) comes from the entry name
        specified in the subprogram_renaming_declaration.


     NOTES
27   (22) A task entry has corresponding accept_statements (zero or more),
     whereas a protected entry has a corresponding entry_body (exactly one).

28   (23) A consequence of the rule regarding the allowed placements of
     accept_statements is that a task can execute accept_statements only for
     its own entries.

29   (24) A return_statement (see 6.5) or a requeue_statement (see 9.5.4) may
     be used to complete the execution of an accept_statement or an entry_
     body.

   29.a   Ramification:  An accept_statement need not have a handled_
        sequence_of_statements even if the corresponding entry has
        parameters.  Equally, it can have a handled_sequence_of_statements
        even if the corresponding entry has no parameters.

   29.b   Ramification:  A single entry overloads a subprogram, an
        enumeration literal, or another single entry if they have the same
        defining_identifier.  Overloading is not allowed for entry family
        names.  A single entry or an entry of an entry family can be renamed
        as a procedure as explained in 8.5.4.

30   (25) The condition in the entry_barrier may reference anything visible
     except the formal parameters of the entry.  This includes the entry
     index (if any), the components (including discriminants) of the
     protected object, the Count attribute of an entry of that protected
     object, and data global to the protected unit.

     31   The restriction against referencing the formal parameters within an
     entry_barrier ensures that all calls of the same entry see the same
     barrier value.  If it is necessary to look at the parameters of an entry
     call before deciding whether to handle it, the entry_barrier can be
     ``when True'' and the caller can be requeued (on some private entry)
     when its parameters indicate that it cannot be handled immediately.


                                  Examples

32   Examples of entry declarations:

33  entry Read(V : out Item);
    entry Seize;
    entry Request(Level)(D : Item);  --  a family of entries

34   Examples of accept statements:

35  accept Shut_Down;

36  accept Read(V : out Item) do
       V := Local_Item;
    end Read;

37  accept Request(Low)(D : Item) do
       ...
    end Request;


                            Extensions to Ada 83

        37.a   {extensions to Ada 83} The syntax rule for entry_body is new.

        37.b   Accept_statements can now have exception_handlers.



9.5.3 Entry Calls

1   {entry call} [An entry_call_statement (an entry call) can appear in
various contexts.]  {simple entry call} {entry call (simple)} A simple entry
call is a stand-alone statement that represents an unconditional call on an
entry of a target task or a protected object.  [Entry calls can also appear
as part of select_statements (see 9.7).]


                                   Syntax

2   entry_call_statement ::= entry_name [actual_parameter_part];


                            Name Resolution Rules

3   The entry_name given in an entry_call_statement shall resolve to denote
an entry.  The rules for parameter associations are the same as for
subprogram calls (see 6.4 and 6.4.1).


                              Static Semantics

4   [The entry_name of an entry_call_statement specifies (explicitly or
implicitly) the target object of the call, the entry or entry family, and the
entry index, if any (see 9.5).]
                              Dynamic Semantics

5   {open entry} {entry (open)} {closed entry} {entry (closed)} Under certain
circumstances (detailed below), an entry of a task or protected object is
checked to see whether it is open or closed:

    6  {open entry (of a task)} {closed entry (of a task)} An entry of a
       task is open if the task is blocked on an accept_statement that
       corresponds to the entry (see 9.5.2), or on a selective_accept
       (see 9.7.1) with an open accept_alternative that corresponds to
       the entry; otherwise it is closed.

    7  {open entry (of a protected object)} {closed entry (of a
       protected object)} An entry of a protected object is open if the
       condition of the entry_barrier of the corresponding entry_body
       evaluates to True; otherwise it is closed.  {Program_Error
       (raised by failure of run-time check)} If the evaluation of the
       condition propagates an exception, the exception Program_Error is
       propagated to all current callers of all entries of the protected
       object.

 7.a    Reason:  An exception during barrier evaluation is considered
        essentially a fatal error.  All current entry callers are
        notified with a Program_Error.  In a fault-tolerant system, a
        protected object might provide a Reset protected procedure, or
        equivalent, to support attempts to restore such a "broken"
        protected object to a reasonable state.

        7.b   Discussion:  Note that the definition of when a task entry is
        open is based on the state of the (accepting) task, whereas the
        "openness" of a protected entry is defined only when it is explicitly
        checked, since the barrier expression needs to be evaluated.
        Implementation permissions are given (below) to allow implementations
        to evaluate the barrier expression more or less often than it is
        checked, but the basic semantic model presumes it is evaluated at the
        times when it is checked.

8   {execution [entry_call_statement]} For the execution of an entry_call_
statement, evaluation of the name and of the parameter associations is as for
a subprogram call (see 6.4).  {issue (an entry call)} The entry call is then
issued:  For a call on an entry of a protected object, a new protected action
is started on the object (see 9.5.1).  The named entry is checked to see if
it is open; {select an entry call (immediately)} if open, the entry call is
said to be selected immediately, and the execution of the call proceeds as
follows:

    9  For a call on an open entry of a task, the accepting task becomes
       ready and continues the execution of the corresponding accept_
       statement (see 9.5.2).

   10  For a call on an open entry of a protected object, the
       corresponding entry_body is executed (see 9.5.2) as part of the
       protected action.

11   If the accept_statement or entry_body completes other than by a requeue
(see 9.5.4), return is made to the caller (after servicing the entry queues
-- see below); any necessary assigning back of formal to actual parameters
occurs, as for a subprogram call (see 6.4.1); such assignments take place
outside of any protected action.

        11.a   Ramification:  The return to the caller will generally not
        occur until the protected action completes, unless some other thread
        of control is given the job of completing the protected action and
        releasing the associated execution resource.

12   If the named entry is closed, the entry call is added to an entry queue
(as part of the protected action, for a call on a protected entry), and the
call remains queued until it is selected or cancelled; {entry queue} there is
a separate (logical) entry queue for each entry of a given task or protected
object [(including each entry of an entry family)].

13   {service (an entry queue)} {select an entry call (from an entry queue)}
When a queued call is selected, it is removed from its entry queue.
Selecting a queued call from a particular entry queue is called servicing the
entry queue.  An entry with queued calls can be serviced under the following
circumstances:

   14  When the associated task reaches a corresponding accept_
       statement, or a selective_accept with a corresponding open
       accept_alternative;

   15  If after performing, as part of a protected action on the
       associated protected object, an operation on the object other
       than a call on a protected function, the entry is checked and
       found to be open.

16   {select an entry call (from an entry queue)} If there is at least one
call on a queue corresponding to an open entry, then one such call is
selected according to the entry queuing policy in effect (see below), and the
corresponding accept_statement or entry_body is executed as above for an
entry call that is selected immediately.

17   {entry queuing policy} The entry queuing policy controls selection among
queued calls both for task and protected entry queues.  {default entry
queuing policy} {entry queuing policy (default policy)} The default entry
queuing policy is to select calls on a given entry queue in order of arrival.
If calls from two or more queues are simultaneously eligible for selection,
the default entry queuing policy does not specify which queue is serviced
first.  Other entry queuing policies can be specified by pragmas (see D.4).

18   For a protected object, the above servicing of entry queues continues
until there are no open entries with queued calls, at which point the
protected action completes.

        18.a   Discussion:  While servicing the entry queues of a protected
        object, no new calls can be added to any entry queue of the object,
        except due to an internal requeue (see 9.5.4).  This is because the
        first step of a call on a protected entry is to start a new protected
        action, which implies acquiring (for exclusive read-write access) the
        execution resource associated with the protected object, which cannot
        be done while another protected action is already in progress.

19   {blocked [during an entry call]} For an entry call that is added to a
queue, and that is not the triggering_statement of an asynchronous_select
(see 9.7.4), the calling task is blocked until the call is cancelled, or the
call is selected and a corresponding accept_statement or entry_body completes
without requeuing.  In addition, the calling task is blocked during a
rendezvous.  {94-4776.d}

        19.a   Ramification:  For a call on a protected entry, the caller is
        not blocked if the call is selected immediately, unless a requeue
        causes the call to be queued.

20   {cancellation (of an entry call)} An attempt can be made to cancel an
entry call upon an abort (see 9.8) and as part of certain forms of select_
statement (see 9.7.2, 9.7.3, and 9.7.4).  The cancellation does not take
place until a point (if any) when the call is on some entry queue, and not
protected from cancellation as part of a requeue (see 9.5.4); at such a
point, the call is removed from the entry queue and the call completes due to
the cancellation.  The cancellation of a call on an entry of a protected
object is a protected action[, and as such cannot take place while any other
protected action is occurring on the protected object.  Like any protected
action, it includes servicing of the entry queues (in case some entry barrier
depends on a Count attribute).]

        20.a   Implementation Note:  In the case of an attempted cancellation
        due to abort, this removal might have to be performed by the calling
        task itself if the ceiling priority of the protected object is lower
        than the task initiating the abort.

21   {Tasking_Error (raised by failure of run-time check)} A call on an entry
of a task that has already completed its execution raises the exception
Tasking_Error at the point of the call; similarly, this exception is raised
at the point of the call if the called task completes its execution or
becomes abnormal before accepting the call or completing the rendezvous (see
9.8).  This applies equally to a simple entry call and to an entry call as
part of a select_statement.


                         Implementation Permissions

22   An implementation may perform the sequence of steps of a protected
action using any thread of control; it need not be that of the task that
started the protected action.  If an entry_body completes without requeuing,
then the corresponding calling task may be made ready without waiting for the
entire protected action to complete.

        22.a   Reason:  These permissions are intended to allow flexibility
        for implementations on multiprocessors.  On a monoprocessor, which
        thread of control executes the protected action is essentially
        invisible, since the thread is not abortable in any case, and the
        "current_task" function is not guaranteed to work during a protected
        action (see C.7).

23   When the entry of a protected object is checked to see whether it is
open, the implementation need not reevaluate the condition of the
corresponding entry_barrier if no variable or attribute referenced by the
condition (directly or indirectly) has been altered by the execution (or
cancellation) of a protected procedure or entry call on the object since the
condition was last evaluated.

        23.a   Ramification:  Changes to variables referenced by an entry
        barrier that result from actions outside of a protected procedure or
        entry call on the protected object need not be "noticed."  For
        example, if a global variable is referenced by an entry barrier, it
        should not be altered (except as part of a protected action on the
        object) any time after the barrier is first evaluated.  In other
        words, globals can be used to "parameterize" a protected object, but
        they cannot reliably be used to control it after the first use of the
        protected object.

        23.b   Implementation Note:  Note that even if a global variable is
        volatile, the implementation need only reevaluate a barrier if the
        global is updated during a protected action on the protected object.
        This ensures that an entry-open bit-vector implementation approach is
        possible, where the bit-vector is computed at the end of a protected
        action, rather than upon each entry call.

24   An implementation may evaluate the conditions of all entry_barriers of a
given protected object any time any entry of the object is checked to see if
it is open.

        24.a   Ramification:  In other words, any side-effects of evaluating
        an entry barrier should be innocuous, since an entry barrier might be
        evaluated more or less often than is implied by the "official"
        dynamic semantics.

        24.b   Implementation Note:  It is anticipated that when the number
        of entries is known to be small, all barriers will be evaluated any
        time one of them needs to be, to produce an "entry-open bit-vector."
        The appropriate bit will be tested when the entry is called, and only
        if the bit is false will a check be made to see whether the
        bit-vector might need to be recomputed.  This should allow an
        implementation to maximize the performance of a call on an open
        entry, which seems like the most important case.

        24.c   In addition to the entry-open bit-vector, an "is-valid" bit is
        needed per object, which indicates whether the current bit-vector
        setting is valid.  A "depends-on-Count-attribute" bit is needed per
        type.  The "is-valid" bit is set to false (as are all the bits of the
        bit-vector) when the protected object is first created, as well as
        any time an exception is propagated from computing the bit-vector.
        Is-valid would also be set false any time the Count is changed and
        "depends-on-Count-attribute" is true for the type, or a protected
        procedure or entry returns indicating it might have updated a
        variable referenced in some barrier.

        24.d   A single procedure can be compiled to evaluate all of the
        barriers, set the entry-open bit-vector accordingly, and set the
        is-valid bit to true.  It could have a "when others" handler to set
        them all false, and call a routine to propagate Program_Error to all
        queued callers.

        24.e   For protected types where the number of entries is not known
        to be small, it makes more sense to evaluate a barrier only when the
        corresponding entry is checked to see if it is open.  It isn't worth
        saving the state of the entry between checks, because of the space
        that would be required.  Furthermore, the entry queues probably want
        to take up space only when there is actually a caller on them, so
        rather than an array of all entry queues, a linked list of nonempty
        entry queues make the most sense in this case, with the first caller
        on each entry queue acting as the queue header.

25   When an attempt is made to cancel an entry call, the implementation need
not make the attempt using the thread of control of the task (or interrupt)
that initiated the cancellation; in particular, it may use the thread of
control of the caller itself to attempt the cancellation, even if this might
allow the entry call to be selected in the interim.

        25.a   Reason:  Because cancellation of a protected entry call is a
        protected action (which helps make the Count attribute of a protected
        entry meaningful), it might not be practical to attempt the
        cancellation from the thread of control that initiated the
        cancellation.  For example, if the cancellation is due to the
        expiration of a delay, it is unlikely that the handler of the timer
        interrupt could perform the necessary protected action itself (due to
        being on the interrupt level).  Similarly, if the cancellation is due
        to an abort, it is possible that the task initiating the abort has a
        priority higher than the ceiling priority of the protected object
        (for implementations that support ceiling priorities).  Similar
        considerations could apply in a multiprocessor situation.


     NOTES
26   (26) If an exception is raised during the execution of an entry_body, it
     is propagated to the corresponding caller (see 11.4).

27   (27) For a call on a protected entry, the entry is checked to see if it
     is open prior to queuing the call, and again thereafter if its Count
     attribute (see 9.9) is referenced in some entry barrier.

   27.a   Ramification:  Given this, extra care is required if a reference to
        the Count attribute of an entry appears in the entry's own barrier.

   27.b   Reason:  An entry is checked to see if it is open prior to queuing
        to maximize the performance of a call on an open entry.

28   (28) In addition to simple entry calls, the language permits timed,
     conditional, and asynchronous entry calls (see 9.7.2, 9.7.3, and see
     9.7.4).

   28.a   Ramification:  A task can call its own entries, but the task will
        deadlock if the call is a simple entry call.

29   (29) The condition of an entry_barrier is allowed to be evaluated by an
     implementation more often than strictly necessary, even if the
     evaluation might have side effects.  On the other hand, an
     implementation need not reevaluate the condition if nothing it
     references was updated by an intervening protected action on the
     protected object, even if the condition references some global variable
     that might have been updated by an action performed from outside of a
     protected action.


                                  Examples

30   Examples of entry calls:

31  Agent.Shut_Down;                      --  see 9.1
    Parser.Next_Lexeme(E);                --  see 9.1
    Pool(5).Read(Next_Char);              --  see 9.1
    Controller.Request(Low)(Some_Item);   --  see 9.1
    Flags(3).Seize;                       --  see 9.4



9.5.4 Requeue Statements

1   [A requeue_statement can be used to complete an accept_statement or
entry_body, while redirecting the corresponding entry call to a new (or the
same) entry queue.  {requeue} Such a requeue can be performed with or without
allowing an intermediate cancellation of the call, due to an abort or the
expiration of a delay.  {preference control: see requeue} {broadcast signal:
see requeue}]


                                   Syntax

2   requeue_statement ::= requeue entry_name [with abort];


                            Name Resolution Rules

3   {target entry (of a requeue_statement)} The entry_name of a requeue_
statement shall resolve to denote an entry (the target entry) that either has
no parameters, or that has a profile that is type conformant (see 6.3.1) with
the profile of the innermost enclosing entry_body or accept_statement.  {type
conformance (required)}


                               Legality Rules

4   A requeue_statement shall be within a callable construct that is either
an entry_body or an accept_statement, and this construct shall be the
innermost enclosing body or callable construct.

5   If the target entry has parameters, then its profile shall be subtype
conformant with the profile of the innermost enclosing callable construct.
{subtype conformance (required)}

6   {accessibility rule [requeue statement]} In a requeue_statement of an
accept_statement of some task unit, either the target object shall be a part
of a formal parameter of the accept_statement, or the accessibility level of
the target object shall not be equal to or statically deeper than any
enclosing accept_statement of the task unit.  In a requeue_statement of an
entry_body of some protected unit, either the target object shall be a part
of a formal parameter of the entry_body, or the accessibility level of the
target object shall not be statically deeper than that of the entry_
declaration.  {94-4715.a} {94-4828.c}

        6.a   Ramification:  In the entry_body case, the intent is that the
        target object can be global, or can be a component of the protected
        unit, but cannot be a local variable of the entry_body.

        6.b   Reason:  These restrictions ensure that the target object of
        the requeue outlives the completion and finalization of the enclosing
        callable construct.  They also prevent requeuing from a nested
        accept_statement on a parameter of an outer accept_statement, which
        could create some strange "long-distance" connections between an
        entry caller and its server.

        6.c   Note that in the strange case where a task_body is nested
        inside an accept_statement, it is permissible to requeue from an
        accept_statement of the inner task_body on parameters of the outer
        accept_statement.  This is not a problem because all calls on the
        inner task have to complete before returning from the outer accept_
        statement, meaning no "dangling calls" will be created.

        6.d   Implementation Note:  By disallowing certain requeues, we
        ensure that the normal terminate_alternative rules remain sensible,
        and that explicit clearing of the entry queues of a protected object
        during finalization is rarely necessary.  In particular, such
        clearing of the entry queues is necessary only (ignoring premature
        Unchecked_Deallocation) for protected objects declared in a task_body
        (or created by an allocator for an access type declared in such a
        body) containing one or more requeue_statements.  Protected objects
        declared in subprograms, or at the library level, will never need to
        have their entry queues explicitly cleared during finalization.


                              Dynamic Semantics

7   {execution [requeue_statement]} The execution of a requeue_statement
proceeds by first evaluating the entry_name[, including the prefix
identifying the target task or protected object and the expression
identifying the entry within an entry family, if any].  The entry_body or
accept_statement enclosing the requeue_statement is then completed[,
finalized, and left (see 7.6.1)].

8   {execution [requeue task entry]} For the execution of a requeue on an
entry of a target task, after leaving the enclosing callable construct, the
named entry is checked to see if it is open and the requeued call is either
selected immediately or queued, as for a normal entry call (see 9.5.3).

9   {execution [requeue protected entry]} For the execution of a requeue on
an entry of a target protected object, after leaving the enclosing callable
construct:

   10  if the requeue is an internal requeue (that is, the requeue is
       back on an entry of the same protected object -- see 9.5), the
       call is added to the queue of the named entry and the ongoing
       protected action continues (see 9.5.1);

 10.a   Ramification:  Note that for an internal requeue, the call is
        queued without checking whether the target entry is open.  This
        is because the entry queues will be serviced before the current
        protected action completes anyway, and considering the requeued
        call immediately might allow it to "jump" ahead of existing
        callers on the same queue.

   11  if the requeue is an external requeue (that is, the target
       protected object is not implicitly the same as the current object
       -- see 9.5), a protected action is started on the target object
       and proceeds as for a normal entry call (see 9.5.3).

12   If the new entry named in the requeue_statement has formal parameters,
then during the execution of the accept_statement or entry_body corresponding
to the new entry, the formal parameters denote the same objects as did the
corresponding formal parameters of the callable construct completed by the
requeue.  [In any case, no parameters are specified in a requeue_statement;
any parameter passing is implicit.]

13   {requeue-with-abort} If the requeue_statement includes the reserved
words with abort (it is a requeue-with-abort), then:

   14  if the original entry call has been aborted (see 9.8), then the
       requeue acts as an abort completion point for the call, and the
       call is cancelled and no requeue is performed;

   15  if the original entry call was timed (or conditional), then the
       original expiration time is the expiration time for the requeued
       call.

16   If the reserved words with abort do not appear, then the call remains
protected against cancellation while queued as the result of the requeue_
statement.

        16.a   Ramification:  This protection against cancellation lasts only
        until the call completes or a subsequent requeue-with-abort is
        performed on the call.

        16.b   Reason:  We chose to protect a requeue, by default, against
        abort or cancellation.  This seemed safer, since it is likely that
        extra steps need to be taken to allow for possible cancellation once
        the servicing of an entry call has begun.  This also means that in
        the absence of with abort the usual Ada 83 behavior is preserved,
        namely that once an entry call is accepted, it cannot be cancelled
        until it completes.


     NOTES
17   (30) A requeue is permitted from a single entry to an entry of an entry
     family, or vice-versa.  The entry index, if any, plays no part in the
     subtype conformance check between the profiles of the two entries; an
     entry index is part of the entry_name for an entry of a family.
     {subtype conformance [partial]}


                                  Examples

18   Examples of requeue statements:

19  requeue Request(Medium) with abort;
                        -- requeue on a member of an entry family of the curren\
t task, see 9.1

20  requeue Flags(I).Seize;
                        -- requeue on an entry of an array component, see 9.4


                            Extensions to Ada 83

        20.a   {extensions to Ada 83} The requeue_statement is new.



9.6 Delay Statements, Duration, and Time

1   [{expiration time [partial]} A delay_statement is used to block further
execution until a specified expiration time is reached.  The expiration time
can be specified either as a particular point in time (in a delay_until_
statement), or in seconds from the current time (in a delay_relative_
statement).  The language-defined package Calendar provides definitions for a
type Time and associated operations, including a function Clock that returns
the current time.  {timing: see delay_statement}]


                                   Syntax

2   delay_statement ::= delay_until_statement | delay_relative_statement

3   delay_until_statement ::= delay until delay_expression;

4   delay_relative_statement ::= delay delay_expression;


                            Name Resolution Rules

5   {expected type [delay_relative_statement expression]} The expected type
for the delay_expression in a delay_relative_statement is the predefined type
Duration.  {expected type [delay_until_statement expression]} The
delay_expression in a delay_until_statement is expected to be of any
nonlimited type.


                               Legality Rules

6   {time type} {time base} {clock} There can be multiple time bases, each
with a corresponding clock, and a corresponding time type.  The type of the
delay_expression in a delay_until_statement shall be a time type -- either
the type Time defined in the language-defined package Calendar (see below),
or some other implementation-defined time type (see D.8).

        6.a   Implementation defined:  Any implementation-defined time types.


                              Static Semantics

7   [There is a predefined fixed point type named Duration, declared in the
visible part of package Standard;] a value of type Duration is used to
represent the length of an interval of time, expressed in seconds.  [The type
Duration is not specific to a particular time base, but can be used with any
time base.]

8   A value of the type Time in package Calendar, or of some other
implementation-defined time type, represents a time as reported by a
corresponding clock.

9   The following language-defined library package exists:

10  package Ada.Calendar is
      type Time is private;

11    subtype Year_Number  is Integer range 1901 ..  2099;
      subtype Month_Number is Integer range 1 ..  12;
      subtype Day_Number   is Integer range 1 ..  31;
      subtype Day_Duration is Duration range 0.0 ..  86_400.0;

12    function Clock return Time;

13    function Year   (Date : Time) return Year_Number;
      function Month  (Date : Time) return Month_Number;
      function Day    (Date : Time) return Day_Number;
      function Seconds(Date : Time) return Day_Duration;

14    procedure Split (Date  : in Time;
                       Year    : out Year_Number;
                       Month   : out Month_Number;
                       Day     : out Day_Number;
                       Seconds : out Day_Duration);

15    function Time_Of(Year  : Year_Number;
                       Month   : Month_Number;
                       Day     : Day_Number;
                       Seconds : Day_Duration := 0.0)
       return Time;

16    function "+" (Left : Time;   Right : Duration) return Time;
      function "+" (Left : Duration; Right : Time) return Time;
      function "-" (Left : Time;   Right : Duration) return Time;
      function "-" (Left : Time;   Right : Time) return Duration;

17    function "<" (Left, Right : Time) return Boolean;
      function "<="(Left, Right : Time) return Boolean;
      function ">" (Left, Right : Time) return Boolean;
      function ">="(Left, Right : Time) return Boolean;

18    Time_Error : exception;

19  private
       ... -- not specified by the language
    end Ada.Calendar;


                              Dynamic Semantics

20   {execution [delay_statement]} For the execution of a delay_statement,
the delay_expression is first evaluated.  {expiration time (for a delay_
until_statement)} For a delay_until_statement, the expiration time for the
delay is the value of the delay_expression, in the time base associated with
the type of the expression.  {expiration time (for a delay_relative_
statement)} For a delay_relative_statement, the expiration time is defined as
the current time, in the time base associated with relative delays, plus the
value of the delay_expression converted to the type Duration, and then
rounded up to the next clock tick.  {implicit subtype conversion [delay
expression]} The time base associated with relative delays is as defined in
D.9, ``Delay Accuracy'' or is implementation defined.

        20.a   Implementation defined:  The time base associated with
        relative delays.

        20.b   Ramification:  Rounding up to the next clock tick means that
        the reading of the delay-relative clock when the delay expires should
        be no less than the current reading of the delay-relative clock plus
        the specified duration.

21   {blocked [on a delay_statement]} The task executing a delay_statement is
blocked until the expiration time is reached, at which point it becomes ready
again.  If the expiration time has already passed, the task is not blocked.

        21.a   Discussion:  For a delay_relative_statement, this case
        corresponds to when the value of the delay_expression is zero or
        negative.

        21.b   Even though the task is not blocked, it might be put back on
        the end of its ready queue.  See D.2, ``Priority Scheduling''.

22   {cancellation (of a delay_statement)} If an attempt is made to cancel
the delay_statement [(as part of an asynchronous_select or abort -- see 9.7.4
and 9.8)], the _statement is cancelled if the expiration time has not yet
passed, thereby completing the delay_statement.

        22.a   Reason:  This is worded this way so that in an asynchronous_
        select where the triggering_statement is a delay_statement, an
        attempt to cancel the delay when the abortable_part completes is
        ignored if the expiration time has already passed, in which case the
        optional statements of the triggering_alternative are executed.

23   The time base associated with the type Time of package Calendar is
implementation defined.

        23.a   Implementation defined:  The time base of the type
        Calendar.Time.

The function Clock of package Calendar returns a value representing the
current time for this time base.  [The implementation-defined value of the
named number System.Tick (see 13.7) is an approximation of the length of the
real-time interval during which the value of Calendar.Clock remains
constant.]

24   The functions Year, Month, Day, and Seconds return the corresponding
values for a given value of the type Time, as appropriate to an
implementation-defined timezone; the procedure Split returns all four
corresponding values.  Conversely, the function Time_Of combines a year
number, a month number, a day number, and a duration, into a value of type
Time.  The operators "+" and "-" for addition and subtraction of times and
durations, and the relational operators for times, have the conventional
meaning.

        24.a   Implementation defined:  The timezone used for package
        Calendar operations.

25   If Time_Of is called with a seconds value of 86_400.0, the value
returned is equal to the value of Time_Of for the next day with a seconds
value of 0.0.  The value returned by the function Seconds or through the
Seconds parameter of the procedure Split is always less than 86_400.0.

26   The exception Time_Error is raised by the function Time_Of if the actual
parameters do not form a proper date.  This exception is also raised by the
operators "+" and "-" if the result is not representable in the type Time or
Duration, as appropriate.  This exception is also raised by the function Year
or the procedure Split if the year number of the given date is outside of the
range of the subtype Year_Number.

        26.a   To be honest:  By "proper date" above we mean that the given
        year has a month with the given day.  For example, February 29th is a
        proper date only for a leap year.

        26.b   Reason:  We allow Year and Split to raise Time_Error because
        the arithmetic operators are allowed (but not required) to produce
        times that are outside the range of years from 1901 to 2099.  This is
        similar to the way integer operators may return values outside the
        base range of their type so long as the value is mathematically
        correct.


                         Implementation Requirements

27   The implementation of the type Duration shall allow representation of
time intervals (both positive and negative) up to at least 86400 seconds (one
day); Duration'Small shall not be greater than twenty milliseconds.  The
implementation of the type Time shall allow representation of all dates with
year numbers in the range of Year_Number[; it may allow representation of
other dates as well (both earlier and later).]


                         Implementation Permissions

28   An implementation may define additional time types (see D.8).

29   An implementation may raise Time_Error if the value of a
delay_expression in a delay_until_statement of a select_statement represents
a time more than 90 days past the current time.  The actual limit, if any, is
implementation-defined.

        29.a   Implementation defined:  Any limit on delay_until_statements
        of select_statements.

        29.b   Implementation Note:  This allows an implementation to
        implement select_statement timeouts using a representation that does
        not support the full range of a time type.  In particular 90 days of
        seconds can be represented in 23 bits, allowing a signed 24-bit
        representation for the seconds part of a timeout.  There is no
        similar restriction allowed for stand-alone delay_until_statements,
        as these can be implemented internally using a loop if necessary to
        accommodate a long delay.


                            Implementation Advice

30   Whenever possible in an implementation, the value of Duration'Small
should be no greater than 100 microseconds.

        30.a   Implementation Note:  This can be satisfied using a 32-bit 2's
        complement representation with a small of 2.0**(-14) -- that is, 61
        microseconds -- and a range of +/- 2.0**17 -- that is, 131_072.0.

31   The time base for delay_relative_statements should be monotonic; it need
not be the same time base as used for Calendar.Clock.


     NOTES
32   (31) A delay_relative_statement with a negative value of the
     delay_expression is equivalent to one with a zero value.

33   (32) A delay_statement may be executed by the environment task;
     consequently delay_statements may be executed as part of the elaboration
     of a library_item or the execution of the main subprogram.  Such
     statements delay the environment task (see 10.2).

34   (33) {potentially blocking operation [delay_statement]} {blocking,
     potentially [delay_statement]} A delay_statement is an abort completion
     point and a potentially blocking operation, even if the task is not
     actually blocked.

35   (34) There is no necessary relationship between System.Tick (the
     resolution of the clock of package Calendar) and Duration'Small (the
     small of type Duration).

   35.a   Ramification:  The inaccuracy of the delay_statement has no
        relation to System.Tick.  In particular, it is possible that the
        clock used for the delay_statement is less accurate than
        Calendar.Clock.

   35.b   We considered making Tick a run-time-determined quantity, to allow
        for easier configurability.  However, this would not be upward
        compatible, and the desired configurability can be achieved using
        functionality defined in Annex D, ``Real-Time Systems''.

36   (35) Additional requirements associated with delay_statements are given
     in D.9, ``Delay Accuracy''.


                                  Examples

37   Example of a relative delay statement:

38  delay 3.0;  -- delay 3.0 seconds

39   {periodic task (example)} {periodic task: see delay_until_statement}
Example of a periodic task:

40  declare
       use Ada.Calendar;
       Next_Time : Time := Clock + Period;
                          -- Period is a global constant of type Duration
    begin
       loop               -- repeated every Period seconds
          delay until Next_Time;
          ... -- perform some actions
          Next_Time := Next_Time + Period;
       end loop;
    end;


                         Inconsistencies With Ada 83

        40.a   {inconsistencies with Ada 83} For programs that raise Time_
        Error on "+" or "-" in Ada 83,the exception might be deferred until a
        call on Split or Year_Number, or might not be raised at all (if the
        offending time is never Split after being calculated).  This should
        not affect typical programs, since they deal only with times
        corresponding to the relatively recent past or near future.

                            Extensions to Ada 83

        40.b   {extensions to Ada 83} The syntax rule for delay_statement is
        modified to allow delay_until_statements.

        40.c   The type Time may represent dates with year numbers outside of
        Year_Number.  Therefore, the operations "+" and "-" need only raise
        Time_Error if the result is not representable in Time (or Duration);
        also, Split or Year will now raise Time_Error if the year number is
        outside of Year_Number.  This change is intended to simplify the
        implementation of "+" and "-" (allowing them to depend on overflow
        for detecting when to raise Time_Error) and to allow local timezone
        information to be considered at the time of Split rather than Clock
        (depending on the implementation approach).  For example, in a POSIX
        environment, it is natural for the type Time to be based on GMT, and
        the results of procedure Split (and the functions Year, Month, Day,
        and Seconds) to depend on local time zone information.  In other
        environments, it is more natural for the type Time to be based on the
        local time zone, with the results of Year, Month, Day, and Seconds
        being pure functions of their input.

        40.d   We anticipate that implementations will provide child packages
        of Calendar to provide more explicit control over time zones and
        other environment-dependent time-related issues.  These would be
        appropriate for standardization in a given environment (such as
        POSIX).



9.7 Select Statements

1   [There are four forms of the select_statement.  One form provides a
selective wait for one or more select_alternatives.  Two provide timed and
conditional entry calls.  The fourth provides asynchronous transfer of
control.]
                                   Syntax

2   select_statement ::=
       selective_accept
      | timed_entry_call
      | conditional_entry_call
      | asynchronous_select


                                  Examples

3   Example of a select statement:

4   select
       accept Driver_Awake_Signal;
    or
       delay 30.0*Seconds;
       Stop_The_Train;
    end select;


                            Extensions to Ada 83

        4.a   {extensions to Ada 83} Asynchronous_select is new.



9.7.1 Selective Accept

1   [This form of the select_statement allows a combination of waiting for,
and selecting from, one or more alternatives.  The selection may depend on
conditions associated with each alternative of the selective_accept.
{time-out: see selective_accept}]


                                   Syntax

2   selective_accept ::=
      select
       [guard]
         select_alternative
    { or
       [guard]
         select_alternative }
    [ else
       sequence_of_statements ]
      end select;

3   guard ::= when condition =>

4   select_alternative ::=
       accept_alternative
      | delay_alternative
      | terminate_alternative

5   accept_alternative ::=
      accept_statement [sequence_of_statements]

6   delay_alternative ::=
      delay_statement [sequence_of_statements]

7   terminate_alternative ::= terminate;

    8   A selective_accept shall contain at least one accept_alternative.  In
    addition, it can contain:

        9  a terminate_alternative (only one); or

       10  one or more delay_alternatives; or

       11  {else part (of a selective_accept)} an else part (the
           reserved word else followed by a sequence_of_statements).

    12   These three possibilities are mutually exclusive.


                               Legality Rules

13   If a selective_accept contains more than one delay_alternative, then all
shall be delay_relative_statements, or all shall be delay_until_statements
for the same time type.

        13.a   Reason:  This simplifies the implementation and the
        description of the semantics.


                              Dynamic Semantics

14   {open alternative} A select_alternative is said to be open if it is not
immediately preceded by a guard, or if the condition of its guard evaluates
to True.  It is said to be closed otherwise.

15   {execution [selective_accept]} For the execution of a selective_accept,
any guard conditions are evaluated; open alternatives are thus determined.
For an open delay_alternative, the delay_expression is also evaluated.
Similarly, for an open accept_alternative for an entry of a family, the
entry_index is also evaluated.  These evaluations are performed in an
arbitrary order, except that a delay_expression or entry_index is not
evaluated until after evaluating the corresponding condition, if any.
Selection and execution of one open alternative, or of the else part, then
completes the execution of the selective_accept; the rules for this selection
are described below.

16   Open accept_alternatives are first considered.  Selection of one such
alternative takes place immediately if the corresponding entry already has
queued calls.  If several alternatives can thus be selected, one of them is
selected according to the entry queuing policy in effect (see 9.5.3 and D.4).
When such an alternative is selected, the selected call is removed from its
entry queue and the handled_sequence_of_statements (if any) of the
corresponding accept_statement is executed; after the rendezvous completes
any subsequent sequence_of_statements of the alternative is executed.
{blocked [execution of a selective_accept]} If no selection is immediately
possible (in the above sense) and there is no else part, the task blocks
until an open alternative can be selected.

17   Selection of the other forms of alternative or of an else part is
performed as follows:

   18  An open delay_alternative is selected when its expiration time is
       reached if no accept_alternative or other delay_alternative can
       be selected prior to the expiration time.  If several delay_
       alternatives have this same expiration time, one of them is
       selected according to the queuing policy in effect (see D.4); the
       default queuing policy chooses arbitrarily among the delay_
       alternatives whose expiration time has passed.

   19  The else part is selected and its sequence_of_statements is
       executed if no accept_alternative can immediately be selected; in
       particular, if all alternatives are closed.

   20  An open terminate_alternative is selected if the conditions
       stated at the end of clause 9.3 are satisfied.

 20.a   Ramification:  In the absence of a requeue_statement, the
        conditions stated are such that a terminate_alternative cannot
        be selected while there is a queued entry call for any entry of
        the task.  In the presence of requeues from a task to one of its
        subtasks, it is possible that when a terminate_alternative of
        the subtask is selected, requeued calls (for closed entries
        only) might still be queued on some entry of the subtask.
        Tasking_Error will be propagated to such callers, as is usual
        when a task completes while queued callers remain.

21   {Program_Error (raised by failure of run-time check)} The exception
Program_Error is raised if all alternatives are closed and there is no else
part.


     NOTES
22   (36) A selective_accept is allowed to have several open delay_
     alternatives.  A selective_accept is allowed to have several open
     accept_alternatives for the same entry.


                                  Examples

23   Example of a task body with a selective accept:

24  task body Server is
       Current_Work_Item : Work_Item;
    begin
       loop
          select
             accept Next_Work_Item(WI : in Work_Item) do
                Current_Work_Item := WI;
              end;
              Process_Work_Item(Current_Work_Item);
          or
             accept Shut_Down;
             exit;       -- Premature shut down requested
          or
             terminate;  -- Normal shutdown at end of scope
          end select;
       end loop;
    end Server;


                         Wording Changes From Ada 83

        24.a   The name of selective_wait was changed to selective_accept to
        better describe what is being waited for.  We kept select_alternative
        as is, because selective_accept_alternative was too easily confused
        with accept_alternative.



9.7.2 Timed Entry Calls

1   [A timed_entry_call issues an entry call that is cancelled if the call
(or a requeue-with-abort of the call) is not selected before the expiration
time is reached.  {time-out: see timed_entry_call}]


                                   Syntax

2   timed_entry_call ::=
      select
       entry_call_alternative
      or
       delay_alternative
      end select;

3   entry_call_alternative ::=
      entry_call_statement [sequence_of_statements]


                              Dynamic Semantics

4   {execution [timed_entry_call]} For the execution of a timed_entry_call,
the entry_name and the actual parameters are evaluated, as for a simple entry
call (see 9.5.3).  The expiration time (see 9.6) for the call is determined
by evaluating the delay_expression of the delay_alternative; the entry call
is then issued.

5   If the call is queued (including due to a requeue-with-abort), and not
selected before the expiration time is reached, an attempt to cancel the call
is made.  If the call completes due to the cancellation, the optional
sequence_of_statements of the delay_alternative is executed; if the entry
call completes normally, the optional sequence_of_statements of the entry_
call_alternative is executed.

        5.a   Ramification:  The fact that the syntax calls for an entry_
        call_statement means that this fact is used in overload resolution.
        For example, if there is a procedure X and an entry X (both with no
        parameters), then "select X; ..." is legal, because overload
        resolution knows that the entry is the one that was meant.


                                  Examples

6   Example of a timed entry call:

7   select
       Controller.Request(Medium)(Some_Item);
    or
       delay 45.0;
       --  controller too busy, try something else
    end select;


                         Wording Changes From Ada 83

        7.a   This clause comes before the one for Conditional Entry Calls,
        so we can define conditional entry calls in terms of timed entry
        calls.



9.7.3 Conditional Entry Calls

1   [A conditional_entry_call issues an entry call that is then cancelled if
it is not selected immediately (or if a requeue-with-abort of the call is not
selected immediately).]

        1.a   To be honest:  In the case of an entry call on a protected
        object, it is OK if the entry is closed at the start of the
        corresponding protected action, so long as it opens and the call is
        selected before the end of that protected action (due to changes in
        the Count attribute).


                                   Syntax

2   conditional_entry_call ::=
      select
       entry_call_alternative
      else
       sequence_of_statements
      end select;


                              Dynamic Semantics

3   {execution [conditional_entry_call]} The execution of a conditional_
entry_call is defined to be equivalent to the execution of a timed_entry_call
with a delay_alternative specifying an immediate expiration time and the same
sequence_of_statements as given after the reserved word else.


     NOTES
4    (37) A conditional_entry_call may briefly increase the Count attribute
     of the entry, even if the conditional call is not selected.


                                  Examples

5   Example of a conditional entry call:

6   procedure Spin(R : in Resource) is
    begin
       loop
          select
             R.Seize;
             return;
          else
             null;  --  busy waiting
          end select;
       end loop;
    end;


                         Wording Changes From Ada 83

        6.a   This clause comes after the one for Timed Entry Calls, so we
        can define conditional entry calls in terms of timed entry calls.  We
        do that so that an "expiration time" is defined for both, thereby
        simplifying the definition of what happens on a requeue-with-abort.



9.7.4 Asynchronous Transfer of Control

1   [An asynchronous select_statement provides asynchronous transfer of
control upon completion of an entry call or the expiration of a delay.]


                                   Syntax

2   asynchronous_select ::=
      select
       triggering_alternative
      then abort
       abortable_part
      end select;

3   triggering_alternative ::= triggering_statement [sequence_of_statements]

4   triggering_statement ::= entry_call_statement | delay_statement

5   abortable_part ::= sequence_of_statements


                              Dynamic Semantics

6   {execution [asynchronous_select with an entry call trigger]} For the
execution of an asynchronous_select whose triggering_statement is an entry_
call_statement, the entry_name and actual parameters are evaluated as for a
simple entry call (see 9.5.3), and the entry call is issued.  If the entry
call is queued (or requeued-with-abort), then the abortable_part is executed.
[If the entry call is selected immediately, and never requeued-with-abort,
then the abortable_part is never started.]

7   {execution [asynchronous_select with a delay_statement trigger]} For the
execution of an asynchronous_select whose triggering_statement is a delay_
statement, the delay_expression is evaluated and the expiration time is
determined, as for a normal delay_statement.  If the expiration time has not
already passed, the abortable_part is executed.

8   If the abortable_part completes and is left prior to completion of the
triggering_statement, an attempt to cancel the triggering_statement is made.
If the attempt to cancel succeeds (see 9.5.3 and 9.6), the asynchronous_
select is complete.

9   If the triggering_statement completes other than due to cancellation, the
abortable_part is aborted (if started but not yet completed -- see 9.8).  If
the triggering_statement completes normally, the optional sequence_of_
statements of the triggering_alternative is executed after the abortable_part
is left.

        9.a   Discussion:  We currently don't specify when the by-copy [in]
        out parameters are assigned back into the actuals.  We considered
        requiring that to happen after the abortable_part is left.  However,
        that doesn't seem useful enough to justify possibly overspecifying
        the implementation approach, since some of the parameters are passed
        by reference anyway.

        9.b   In an earlier description, we required that the sequence_of_
        statements of the triggering_alternative execute after aborting the
        abortable_part, but before waiting for it to complete and finalize,
        to provide more rapid response to the triggering event in case the
        finalization was unbounded.  However, various reviewers felt that
        this created unnecessary complexity in the description, and a
        potential for undesirable concurrency (and nondeterminism) within a
        single task.  We have now reverted to simpler, more deterministic
        semantics, but anticipate that further discussion of this issue might
        be appropriate during subsequent reviews.  One possibility is to
        leave this area implementation defined, so as to encourage
        experimentation.  The user would then have to assume the worst about
        what kinds of actions are appropriate for the sequence_of_statements
        of the triggering_alternative to achieve portability.


                                  Examples

10   {signal handling (example)} {interrupt (example using asynchronous_
select)} {terminal interrupt (example)} Example of a main command loop for a
command interpreter:

11  loop
        select
            Terminal.Wait_For_Interrupt;
            Put_Line("Interrupted");
        then abort
            -- This will be abandoned upon terminal interrupt
            Put_Line("-> ");
            Get_Line(Command, Last);
            Process_Command(Command(1..Last));
        end select;
    end loop;

12   Example of a time-limited calculation:  {time-out: see asynchronous_
select} {time-out (example)} {time limit (example)} {interrupt (example using
asynchronous_select)} {timer interrupt (example)}

13  select
       delay 5.0;
       Put_Line("Calculation does not converge");
    then abort
       -- This calculation should finish in 5.0 seconds;
       --  if not, it is assumed to diverge.
       Horribly_Complicated_Recursive_Function(X, Y);
    end select;


                            Extensions to Ada 83

        13.a   {extensions to Ada 83} Asynchronous_select is new.



9.8 Abort of a Task - Abort of a Sequence of Statements

1   [An abort_statement causes one or more tasks to become abnormal, thus
preventing any further interaction with such tasks.  The completion of the
triggering_statement of an asynchronous_select causes a sequence_of_
statements to be aborted.]


                                   Syntax

2   abort_statement ::= abort task_name {, task_name};


                            Name Resolution Rules

3   {expected type [abort_statement task_name]} Each task_name is expected to
be of any task type[; they need not all be of the same task type.]


                              Dynamic Semantics

4   {execution [abort_statement]} For the execution of an abort_statement,
the given task_names are evaluated in an arbitrary order.  {abort (of a
task)} {abnormal task} {task state [abnormal]} Each named task is then
aborted, which consists of making the task abnormal and aborting the
execution of the corresponding task_body, unless it is already completed.

        4.a   Ramification:  Note that aborting those tasks is not defined to
        be an abort-deferred operation.  Therefore, if one of the named tasks
        is the task executing the abort_statement, or if the task executing
        the abort_statement depends on one of the named tasks, then it is
        possible for the execution of the abort_statement to be aborted, thus
        leaving some of the tasks unaborted.  This allows the implementation
        to use either a sequence of calls to an ``abort task'' RTS primitive,
        or a single call to an ``abort list of tasks'' RTS primitive.

5   {execution [aborting the execution of a construct]} {abort (of the
execution of a construct)} When the execution of a construct is aborted
(including that of a task_body or of a sequence_of_statements), the execution
of every construct included within the aborted execution is also aborted,
except for executions included within the execution of an abort-deferred
operation; the execution of an abort-deferred operation continues to
completion without being affected by the abort; {abort-deferred operation}
the following are the abort-deferred operations:

    6  a protected action;

    7  waiting for an entry call to complete (after having initiated the
       attempt to cancel it -- see below);

    8  waiting for the termination of dependent tasks;

    9  the execution of an Initialize procedure as the last step of the
       default initialization of a controlled object;

   10  the execution of a Finalize procedure as part of the finalization
       of a controlled object;

   11  an assignment operation to an object with a controlled part.

12   [The last three of these are discussed further in 7.6.]

        12.a   Reason:  Deferring abort during Initialize and finalization
        allows, for example, the result of an allocator performed in an
        Initialize operation to be assigned into an access object without
        being interrupted in the middle, which would cause storage leaks.
        For an object with several controlled parts, each individual
        Initialize is abort-deferred.  Note that there is generally no
        semantic difference between making each Finalize abort-deferred,
        versus making a group of them abort-deferred, because if the task
        gets aborted, the first thing it will do is complete any remaining
        finalizations.  Individual objects are finalized prior to an
        assignment operation (if nonlimited controlled) and as part of
        Unchecked_Deallocation.

        12.b   Ramification:  Abort is deferred during the entire assignment
        operation to an object with a controlled part, even if only some
        subcomponents are controlled.  Note that this says "assignment
        operation," not "assignment_statement."  Explicit calls to
        Initialize, Finalize, or Adjust are not abort-deferred.

13   When a master is aborted, all tasks that depend on that master are
aborted.  {94-4715.a}

14   {unspecified [partial]} The order in which tasks become abnormal as the
result of an abort_statement or the abort of a sequence_of_statements is not
specified by the language.

15   If the execution of an entry call is aborted, an immediate attempt is
made to cancel the entry call (see 9.5.3).  If the execution of a construct
is aborted at a time when the execution is blocked, other than for an entry
call, at a point that is outside the execution of an abort-deferred
operation, then the execution of the construct completes immediately.  For an
abort due to an abort_statement, these immediate effects occur before the
execution of the abort_statement completes.  Other than for these immediate
cases, the execution of a construct that is aborted does not necessarily
complete before the abort_statement completes.  However, the execution of the
aborted construct completes no later than its next abort completion point (if
any) that occurs outside of an abort-deferred operation; {abort completion
point} the following are abort completion points for an execution:

   16  the point where the execution initiates the activation of another
       task;

   17  the end of the activation of a task;

   18  the start or end of the execution of an entry call, accept_
       statement, delay_statement, or abort_statement;

 18.a   Ramification:  Although the abort completion point doesn't occur
        until the end of the entry call or delay_statement, these
        operations might be cut short because an abort attempts to
        cancel them.

   19  the start of the execution of a select_statement, or of the
       sequence_of_statements of an exception_handler.

 19.a   Reason:  The start of an exception_handler is considered an
        abort completion point simply because it is easy for an
        implementation to check at such points.

 19.b   Implementation Note:  Implementations may of course check for
        abort more often than at each abort completion point; ideally, a
        fully preemptive implementation of abort will be provided.  If
        preemptive abort is not supported in a given environment, then
        supporting the checking for abort as part of subprogram calls
        and loop iterations might be a useful option.


                          Bounded (Run-Time) Errors

20   {bounded error} An attempt to execute an asynchronous_select as part of
the execution of an abort-deferred operation is a bounded error.  Similarly,
an attempt to create a task that depends on a master that is included
entirely within the execution of an abort-deferred operation is a bounded
error.  {94-4715.a} {Program_Error (raised by failure of run-time check)} In
both cases, Program_Error is raised if the error is detected by the
implementation; otherwise the operations proceed as they would outside an
abort-deferred operation, except that an abort of the abortable_part or the
created task might or might not have an effect.

        20.a   Reason:  An asynchronous_select relies on an abort of the
        abortable_part to effect the asynchronous transfer of control.  For
        an asynchronous_select within an abort-deferred operation, the abort
        might have no effect.

        20.b   Creating a task dependent on a master included within an
        abort-deferred operation is considered an error, because such tasks
        could be aborted while the abort-deferred operation was still
        progressing, undermining the purpose of abort-deferral.  Alter-
        natively, we could say that such tasks are abort-deferred for their
        entire execution, but that seems too easy to abuse.  Note that task
        creation is already a bounded error in protected actions, so this
        additional rule only applies to local task creation as part of
        Initialize, Finalize, or Adjust.


                             Erroneous Execution

21   {erroneous execution} {normal state of an object [partial]} {abnormal
state of an object [partial]} {disruption of an assignment} If an assignment
operation completes prematurely due to an abort, the assignment is said to be
disrupted; the target of the assignment or its parts can become abnormal, and
certain subsequent uses of the object can be erroneous, as explained in
13.9.1.


     NOTES
22   (38) An abort_statement should be used only in situations requiring
     unconditional termination.

23   (39) A task is allowed to abort any task it can name, including itself.

24   (40) Additional requirements associated with abort are given in D.6,
     ``Preemptive Abort''.
                         Wording Changes From Ada 83

        24.a   This clause has been rewritten to accommodate the concept of
        aborting the execution of a construct, rather than just of a task.



9.9 Task and Entry Attributes

                              Dynamic Semantics

1   For a prefix T that is of a task type [(after any implicit dereference)],
the following attributes are defined:

2   T'Callable
                Yields the value True when the task denoted by T is callable,
                and False otherwise; {task state [callable]} {callable} a
                task is callable unless it is completed or abnormal.  The
                value of this attribute is of the predefined type Boolean.

3   T'Terminated
                Yields the value True if the task denoted by T is terminated,
                and False otherwise.  The value of this attribute is of the
                predefined type Boolean.

4   For a prefix E that denotes an entry of a task or protected unit, the
following attribute is defined.  This attribute is only allowed within the
body of the task or protected unit, but excluding, in the case of an entry of
a task unit, within any program unit that is, itself, inner to the body of
the task unit.

5   E'Count
                Yields the number of calls presently queued on the entry E of
                the current instance of the unit.  The value of this
                attribute is of the type universal_integer.


     NOTES
6    (41) For the Count attribute, the entry can be either a single entry or
     an entry of a family.  The name of the entry or entry family can be
     either a direct_name or an expanded name.

7    (42) Within task units, algorithms interrogating the attribute E'Count
     should take precautions to allow for the increase of the value of this
     attribute for incoming entry calls, and its decrease, for example with
     timed_entry_calls.  Also, a conditional_entry_call may briefly increase
     this value, even if the conditional call is not accepted.

8    (43) Within protected units, algorithms interrogating the attribute
     E'Count in the entry_barrier for the entry E should take precautions to
     allow for the evaluation of the condition of the barrier both before and
     after queuing a given caller.



9.10 Shared Variables

                              Static Semantics

1   {shared variable (protection of)} {independently addressable} If two
different objects, including nonoverlapping parts of the same object, are
independently addressable, they can be manipulated concurrently by two
different tasks without synchronization.  Normally, any two nonoverlapping
objects are independently addressable.  However, if packing, record layout,
or Component_Size is specified for a given composite object, then it is
implementation defined whether or not two nonoverlapping parts of that
composite object are independently addressable.

        1.a   Implementation defined:  Whether or not two nonoverlapping
        parts of a composite object are independently addressable, in the
        case where packing, record layout, or Component_Size is specified for
        the object.

        1.b   Implementation Note:  Independent addressability is the only
        high level semantic effect of a pragma Pack.  If two objects are
        independently addressable, the implementation should allocate them in
        such a way that each can be written by the hardware without writing
        the other.  For example, unless the user asks for it, it is generally
        not feasible to choose a bit-packed representation on a machine
        without an atomic bit field insertion instruction, because there
        might be tasks that update neighboring subcomponents concurrently,
        and locking operations on all subcomponents is generally not a good
        idea.

        1.c   Even if packing or one of the other above-mentioned aspects is
        specified, subcomponents should still be updated independently if the
        hardware efficiently supports it.


                              Dynamic Semantics

2   [Separate tasks normally proceed independently and concurrently with one
another.  However, task interactions can be used to synchronize the actions
of two or more tasks to allow, for example, meaningful communication by the
direct updating and reading of variables shared between the tasks.] The
actions of two different tasks are synchronized in this sense when an action
of one task signals an action of the other task; {signal (as defined between
actions)} an action A1 is defined to signal an action A2 under the following
circumstances:

    3  If A1 and A2 are part of the execution of the same task, and the
       language rules require A1 to be performed before A2;

    4  If A1 is the action of an activator that initiates the activation
       of a task, and A2 is part of the execution of the task that is
       activated;

    5  If A1 is part of the activation of a task, and A2 is the action
       of waiting for completion of the activation;

    6  If A1 is part of the execution of a task, and A2 is the action of
       waiting for the termination of the task;

    7  If A1 is the action of issuing an entry call, and A2 is part of
       the corresponding execution of the appropriate entry_body or
       accept_statement.

 7.a    Ramification:  Evaluating the entry_index of an accept_statement
        is not synchronized with a corresponding entry call, nor is
        evaluating the entry barrier of an entry_body.

    8  If A1 is part of the execution of an accept_statement or entry_
       body, and A2 is the action of returning from the corresponding
       entry call;

    9  If A1 is part of the execution of a protected procedure body or
       entry_body for a given protected object, and A2 is part of a
       later execution of an entry_body for the same protected object;

 9.a    Reason:  The underlying principle here is that for one action to
        ``signal'' a second, the second action has to follow a
        potentially blocking operation, whose blocking is dependent on
        the first action in some way.  Protected procedures are not
        potentially blocking, so they can only be "signalers," they
        cannot be signaled.

 9.b    Ramification:  Protected subprogram calls are not defined to
        signal one another, which means that such calls alone cannot be
        used to synchronize access to shared data outside of a protected
        object.

 9.c    Reason:  The point of this distinction is so that on
        multiprocessors with inconsistent caches, the caches only need
        to be refreshed at the beginning of an entry body, and forced
        out at the end of an entry body or protected procedure that
        leaves an entry open.  Protected function calls, and protected
        subprogram calls for entryless protected objects do not require
        full cache consistency.  Entryless protected objects are
        intended to be treated roughly like atomic objects -- each
        operation is indivisible with respect to other operations
        (unless both are reads), but such operations cannot be used to
        synchronize access to other nonvolatile shared variables.

   10  If A1 signals some action that in turn signals A2.


                             Erroneous Execution

11   {erroneous execution} Given an action of assigning to an object, and an
action of reading or updating a part of the same object (or of a neighboring
object if the two are not independently addressable), then the execution of
the actions is erroneous unless the actions are sequential.  {sequential
(actions)} Two actions are sequential if one of the following is true:

   12  One action signals the other;

   13  Both actions occur as part of the execution of the same task;

 13.a   Reason:  Any two actions of the same task are sequential, even
        if one does not signal the other because they can be executed in
        an ``arbitrary'' (but necessarily equivalent to some
        ``sequential'') order.

   14  Both actions occur as part of protected actions on the same
       protected object, and at most one of the actions is part of a
       call on a protected function of the protected object.

 14.a   Reason:  Because actions within protected actions do not always
        imply signaling, we have to mention them here explicitly to make
        sure that actions occurring within different protected actions
        of the same protected object are sequential with respect to one
        another (unless both are part of calls on protected functions).

 14.b   Ramification:  It doesn't matter whether or not the variable
        being assigned is actually a subcomponent of the protected
        object; globals can be safely updated from within the bodies of
        protected procedures or entries.

15   A pragma Atomic or Atomic_Components may also be used to ensure that
certain reads and updates are sequential -- see C.6.

        15.a   Ramification:  If two actions are ``sequential'' it is known
        that their executions don't overlap in time, but it is not
        necessarily specified which occurs first.  For example, all actions
        of a single task are sequential, even though the exact order of
        execution is not fully specified for all constructs.

        15.b   Discussion:  Note that if two assignments to the same variable
        are sequential, but neither signals the other, then the program is
        not erroneous, but it is not specified which assignment ultimately
        prevails.  Such a situation usually corresponds to a programming
        mistake, but in some (rare) cases, the order makes no difference, and
        for this reason this situation is not considered erroneous nor even a
        bounded error.  In Ada 83, this was considered an ``incorrect order
        dependence'' if the ``effect'' of the program was affected, but
        ``effect'' was never fully defined.  In Ada 9X, this situation
        represents a potential nonportability, and a friendly compiler might
        want to warn the programmer about the situation, but it is not
        considered an error.  An example where this would come up would be in
        gathering statistics as part of referencing some information, where
        the assignments associated with statistics gathering don't need to be
        ordered since they are just accumulating aggregate counts, sums,
        products, etc.



9.11 Example of Tasking and Synchronization

                                  Examples

1   The following example defines a buffer protected object to smooth
variations between the speed of output of a producing task and the speed of
input of some consuming task.  For instance, the producing task might have
the following structure:

2   task Producer;

3   task body Producer is
       Char : Character;
    begin
       loop
          ... --  produce the next character Char
          Buffer.Write(Char);
          exit when Char = ASCII.EOT;
       end loop;
    end Producer;

4   and the consuming task might have the following structure:

5   task Consumer;

6   task body Consumer is
       Char : Character;
    begin
       loop
          Buffer.Read(Char);
          exit when Char = ASCII.EOT;
          ... --  consume the character Char
       end loop;
    end Consumer;

7   The buffer object contains an internal pool of characters managed in a
round-robin fashion.  The pool has two indices, an In_Index denoting the
space for the next input character and an Out_Index denoting the space for
the next output character.

8   protected Buffer is
       entry Read (C : out Character);
       entry Write(C : in  Character);
    private
       Pool      : String(1 .. 100);
       Count     : Natural := 0;
       In_Index, Out_Index : Positive := 1;
    end Buffer;

9   protected body Buffer is
       entry Write(C : in Character)
          when Count < Pool'Length is
       begin
          Pool(In_Index) := C;
          In_Index := (In_Index mod Pool'Length) + 1;
          Count    := Count + 1;
       end Write;

10     entry Read(C : out Character)
          when Count > 0 is
       begin
          C := Pool(Out_Index);
          Out_Index := (Out_Index mod Pool'Length) + 1;
          Count     := Count - 1;
       end Read;
    end Buffer;



            Section 10: Program Structure and Compilation Issues


1   [The overall structure of programs and the facilities for separate
compilation are described in this section.  A program is a set of partitions,
each of which may execute in a separate address space, possibly on a separate
computer.

        1.a   Glossary entry:  {Program} A program is a set of partitions,
        each of which may execute in a separate address space, possibly on a
        separate computer.  A partition consists of a set of library units.

        1.b   Glossary entry:  {Partition} A partition is a part of a
        program.  Each partition consists of a set of library units.  Each
        partition may run in a separate address space, possibly on a separate
        computer.  A program may contain just one partition.  A distributed
        program typically contains multiple partitions, which can execute
        concurrently.

2   {library unit (informal introduction)} {library_item (informal
introduction)} {library (informal introduction)} As explained below, a
partition is constructed from library units.  Syntactically, the declaration
of a library unit is a library_item, as is the body of a library unit.  An
implementation may support a concept of a program library (or simply, a
``library''), which contains library_items and their subunits.  {94-4599.a}
{program library: see library} Library units may be organized into a
hierarchy of children, grandchildren, and so on.]

3   This section has two clauses:  10.1, ``Separate Compilation'' discusses
compile-time issues related to separate compilation.  10.2, ``Program
Execution'' discusses issues related to what is traditionally known as ``link
time'' and ``run time'' -- building and executing partitions.


                         Language Design Principles

        3.a   {avoid overspecifying environmental issues} We should avoid
        specifying details that are outside the domain of the language
        itself.  The standard is intended (at least in part) to promote
        portability of Ada programs at the source level.  It is not intended
        to standardize extra-language issues such as how one invokes the
        compiler (or other tools), how one's source is represented and
        organized, version management, the format of error messages, etc.

        3.b   {safe separate compilation} {separate compilation (safe)} The
        rules of the language should be enforced even in the presence of
        separate compilation.  Using separate compilation should not make a
        program less safe.

        3.c   {legality determinable via semantic dependences} It should be
        possible to determine the legality of a compilation unit by looking
        only at the compilation unit itself and the compilation units upon
        which it depends semantically.  As an example, it should be possible
        to analyze the legality of two compilation units in parallel if they
        do not depend semantically upon each other.

        3.d   On the other hand, it may be necessary to look outside that set
        in order to generate code -- this is generally true for generic
        instantiation and inlining, for example.  Also on the other hand, it
        is generally necessary to look outside that set in order to check
        Post-Compilation Rules.

        3.e   See also the ``generic contract model'' Language Design
        Principle of 12.3, ``Generic Instantiation''.

                         Wording Changes From Ada 83

        3.f   The section organization mentioned above is different from that
        of RM83.



10.1 Separate Compilation

1   [{separate compilation} {compilation (separate)} {Program unit} [glossary
entry]A program unit is either a package, a task unit, a protected unit, a
protected entry, a generic unit, or an explicitly declared subprogram other
than an enumeration literal.  Certain kinds of program units can be
separately compiled.  Alternatively, they can appear physically nested within
other program units.

2   {Compilation unit} [glossary entry]The text of a program can be submitted
to the compiler in one or more compilations.  Each compilation is a
succession of compilation_units.  A compilation_unit contains either the
declaration, the body, or a renaming of a program unit.]  The representation
for a compilation is implementation-defined.

        2.a   Implementation defined:  The representation for a compilation.

        2.b   Ramification:  Some implementations might choose to make a
        compilation be a source (text) file.  Others might allow multiple
        source files to be automatically concatenated to form a single
        compilation.  Others still may represent the source in a nontextual
        form such as a parse tree.  Note that the RM9X does not even define
        the concept of a source file.

        2.c   Note that a protected subprogram is a subprogram, and therefore
        a program unit.  An instance of a generic unit is a program unit.

        2.d   A protected entry is a program unit, but protected entries
        cannot be separately compiled.

3   {Library unit} [glossary entry]A library unit is a separately compiled
program unit, and is always a package, subprogram, or generic unit.
{94-4599.f} Library units may have other (logically nested) library units as
children, and may have other program units physically nested within them.
{subsystem} A root library unit, together with its children and grandchildren
and so on, form a subsystem.


                         Implementation Permissions

4   An implementation may impose implementation-defined restrictions on
compilations that contain multiple compilation_units.
        4.a   Implementation defined:  Any restrictions on compilations that
        contain multiple compilation_units.

        4.b   Discussion:  For example, an implementation might disallow a
        compilation that contains two versions of the same compilation unit,
        or that contains the declarations for library packages P1 and P2,
        where P1 precedes P2 in the compilation but P1 has a with_clause that
        mentions P2.


                         Wording Changes From Ada 83

        4.c   The interactions between language issues and environmental
        issues are left open in Ada 9X.  The environment concept is new.  In
        Ada 83, the concept of the program library, for example, appeared to
        be quite concrete, although the rules had no force, since
        implementations could get around them simply by defining various
        mappings from the concept of an Ada program library to whatever data
        structures were actually stored in support of separate compilation.
        Indeed, implementations were encouraged to do so.

        4.d   In RM83, it was unclear which was the official definition of
        ``program unit.''  Definitions appeared in RM83-5, 6, 7, and 9, but
        not 12.  Placing it here seems logical, since a program unit is sort
        of a potential compilation unit.



10.1.1 Compilation Units - Library Units

1   [A library_item is a compilation unit that is the declaration, body, or
renaming of a library unit.  Each library unit (except Standard) has a parent
unit, which is a library package or generic library package.] {child (of a
library unit)} A library unit is a child of its parent unit.  The root
library units are the children of the predefined library package Standard.

        1.a   Ramification:  Standard is a library unit.


                                   Syntax

2   compilation ::= {compilation_unit}

3   compilation_unit ::=
        context_clause library_item
      | context_clause subunit

4   library_item ::= [private] library_unit_declaration
      | library_unit_body
      | [private] library_unit_renaming_declaration

5   library_unit_declaration ::=
         subprogram_declaration | package_declaration
       | generic_declaration    | generic_instantiation

6   library_unit_renaming_declaration ::=
       package_renaming_declaration
     | generic_renaming_declaration
     | subprogram_renaming_declaration

7   library_unit_body ::= subprogram_body | package_body

8   parent_unit_name ::= name


9   {library unit} A library unit is a program unit that is declared by a
library_item.  When a program unit is a library unit, the prefix ``library''
is used to refer to it (or ``generic library'' if generic), as well as to its
declaration and body, as in ``library procedure'', ``library package_body'',
or ``generic library package''.  {compilation unit} The term compilation unit
is used to refer to a compilation_unit.  When the meaning is clear from
context, the term is also used to refer to the library_item of a compilation_
unit or to the proper_body of a subunit [(that is, the compilation_unit
without the context_clause and the separate (parent_unit_name))].

        9.a   Discussion:  In this example:

9.b         with Ada.Text_IO;
            package P is
                ...
            end P;

        9.c   the term ``compilation unit'' can refer to this text: ``with
        Ada.Text_IO; package P is ... end P;'' or to this text:  ``package P
        is ... end P;''.  We use this shorthand because it corresponds to
        common usage.

        9.d   We like to use the word ``unit'' for declaration-plus-body
        things, and ``item'' for declaration or body separately (as in
        declarative_item).  The terms ``compilation_unit,'' ``compilation
        unit,'' and ``subunit'' are exceptions to this rule.  We considered
        changing ``compilation_unit,'' ``compilation unit'' to ``compilation_
        item,'' ``compilation item,'' respectively, but we decided not to.

10   {parent declaration (of a library_item)} {parent declaration (of a
library unit)} The parent declaration of a library_item (and of the library
unit) is the declaration denoted by the parent_unit_name, if any, of the
defining_program_unit_name of the library_item.  {root library unit} If there
is no parent_unit_name, the parent declaration is the declaration of
Standard, the library_item is a root library_item, and the library unit
(renaming) is a root library unit (renaming).  The declaration and body of
Standard itself have no parent declaration.  {parent unit (of a library
unit)} The parent unit of a library_item or library unit is the library unit
declared by its parent declaration.

        10.a   Discussion:  The declaration and body of Standard are presumed
        to exist from the beginning of time, as it were.  There is no way to
        actually write them, since there is no syntactic way to indicate lack
        of a parent.  An attempt to compile a package Standard would result
        in Standard.Standard.

        10.b   Reason:  Library units (other than Standard) have ``parent
        declarations'' and ``parent units''.  Subunits have ``parent
        bodies''.  We didn't bother to define the other possibilities:
        parent body of a library unit, parent declaration of a subunit,
        parent unit of a subunit.  These are not needed, and might get in the
        way of a correct definition of ``child.''

11   [The children of a library unit occur immediately within the declarative
region of the declaration of the library unit.]  {ancestor (of a library
unit)} The ancestors of a library unit are itself, its parent, its parent's
parent, and so on.  [(Standard is an ancestor of every library unit.)]
{descendant} The descendant relation is the inverse of the ancestor relation.

        11.a   Reason:  These definitions are worded carefully to avoid
        defining subunits as children.  Only library units can be children.

        11.b   We use the unadorned term ``ancestors'' here to concisely
        define both ``ancestor unit'' and ``ancestor declaration.''

12   {public library unit} {public declaration of a library unit} {private
library unit} {private declaration of a library unit} A library_unit_
declaration or a library_unit_renaming_declaration is private if the
declaration is immediately preceded by the reserved word private; it is
otherwise public.  A library unit is private or public according to its
declaration.  {public descendant (of a library unit)} The public descendants
of a library unit are the library unit itself, and the public descendants of
its public children.  {private descendant (of a library unit)} Its other
descendants are private descendants.

        12.a   Discussion:  The first concept defined here is that a library_
        item is either public or private (not in relation to anything else --
        it's just a property of the library unit).  The second concept is
        that a library_item is a public descendant or private descendant of a
        given ancestor.  A given library_item can be a public descendant of
        one of its ancestors, but a private descendant of some other
        ancestor.

        12.b   A subprogram declared by a subprogram_body (as opposed to a
        subprogram_declaration) is always public, since the syntax rules
        disallow the reserved word private on a body.

        12.c   Note that a private library unit is a public descendant of
        itself, but a private descendant of its parent.  This is because it
        is visible outside itself -- its privateness means that it is not
        visible outside its parent.

        12.d   Private children of Standard are legal, and follow the normal
        rules.  It is intended that implementations might have some method
        for taking an existing environment, and treating it as a package to
        be ``imported'' into another environment, treating children of
        Standard in the imported environment as children of the imported
        package.

        12.e   Ramification:  Suppose we have a public library unit A, a
        private library unit A.B, and a public library unit A.B.C.  A.B.C is
        a public descendant of itself and of A.B, but a private descendant of
        A; since A.B is private to A, we don't allow A.B.C to escape outside
        A either.  This is similar to the situation that would occur with
        physical nesting, like this:

12.f        package A is
            private
                package B is
                    package C is
                    end C;
                private
                end B;
            end A;

        12.g   Here, A.B.C is visible outside itself and outside A.B, but not
        outside A. (Note that this example is intended to illustrate the
        visibility of program units from the outside; the visibility within
        child units is not quite identical to that of physically nested
        units, since child units are nested after their parent's
        declaration.)


                               Legality Rules

13   The parent unit of a library_item shall be a [library] package or
generic [library] package.

14   If a defining_program_unit_name of a given declaration or body has a
parent_unit_name, then the given declaration or body shall be a library_item.
The body of a program unit shall be a library_item if and only if the
declaration of the program unit is a library_item.  In a library_unit_
renaming_declaration, the [(old)] name shall denote a library_item.
        14.a   Discussion:  We could have allowed nested program units to be
        children of other program units; their semantics would make sense.
        We disallow them to keep things simpler and because they wouldn't be
        particularly useful.

15   A parent_unit_name [(which can be used within a defining_program_unit_
name of a library_item and in the separate clause of a subunit)], and each of
its prefixes, shall not denote a renaming_declaration.  [On the other hand, a
name that denotes a library_unit_renaming_declaration is allowed in a with_
clause and other places where the name of a library unit is allowed.]

16   If a library package is an instance of a generic package, then every
child of the library package shall either be itself an instance or be a
renaming of a library unit.

        16.a   Discussion:  A child of an instance of a given generic unit
        will often be an instance of a (generic) child of the given generic
        unit.  This is not required, however.

        16.b   Reason:  Instances are forbidden from having noninstance
        children for two reasons:

         16.c  We want all source code that can depend on information
               from the private part of a library unit to be inside the
               "subsystem" rooted at the library unit.  If an instance
               of a generic unit were allowed to have a noninstance as a
               child, the source code of that child might depend on
               information from the private part of the generic unit,
               even though it is outside the subsystem rooted at the
               generic unit.

         16.d  Disallowing noninstance children simplifies the descrip-
               tion of the semantics of children of generic packages.

17   A child of a generic library package shall either be itself a generic
unit or be a renaming of some other child of the same generic unit.  The
renaming of a child of a generic package shall occur only within the
declarative region of the generic package.

18   A child of a parent generic package shall be instantiated or renamed
only within the declarative region of the parent generic.

19   For each declaration or renaming of a generic unit as a child of some
parent generic package, there is a corresponding declaration nested
immediately within each instance of the parent.  [This declaration is visible
only within the scope of a with_clause that mentions the child generic unit.]
{94-4933.a} {94-4944.a}

        19.a   Implementation Note:  Within the child, like anything nested
        in a generic unit, one can make up-level references to the current
        instance of its parent, and thereby gain access to the formal
        parameters of the parent, to the types declared in the parent, etc.
        This ``nesting'' model applies even within the generic_formal_part of
        the child, as it does for a generic child of a nongeneric unit.

        19.b   Ramification:  Suppose P is a generic library package, and P.C
        is a generic child of P. P.C can be instantiated inside the
        declarative region of P. Outside P, P.C can be mentioned only in a
        with_clause.  Conceptually, an instance I of P is a package that has
        a nested generic unit called I.C.  Mentioning P.C in a with_clause
        allows I.C to be instantiated.  I need not be a library unit, and the
        instantiation of I.C need not be a library unit.  If I is a library
        unit, and an instance of I.C is a child of I, then this instance has
        to be called something other than C.

20   A library subprogram shall not override a primitive subprogram.

        20.a   Reason:  This prevents certain obscure anomalies.  For
        example, if a library subprogram were to override a subprogram
        declared in its parent package, then in a compilation unit that
        depends indirectly on the library subprogram, the library subprogram
        could hide the overridden operation from all visibility, but the
        library subprogram itself would not be visible.

        20.b   Note that even without this rule, such subprograms would be
        illegal for tagged types, because of the freezing rules.

21   The defining name of a function that is a compilation unit shall not be
an operator_symbol.

        21.a   Reason:  Since overloading is not permitted among compilation
        units, it seems unlikely that it would be useful to define one as an
        operator.  Note that a subunit could be renamed within its parent to
        be an operator.


                              Static Semantics

22   A subprogram_renaming_declaration that is a library_unit_renaming_
declaration is a renaming-as-declaration, not a renaming-as-body.
{94-4625.a} {94-4626.a}

23   [There are two kinds of dependences among compilation units:

   24  The semantic dependences (see below) are the ones needed to check
       the compile-time rules across compilation unit boundaries; a
       compilation unit depends semantically on the other compilation
       units needed to determine its legality.  The visibility rules are
       based on the semantic dependences.

   25  The elaboration dependences (see 10.2) determine the order of
       elaboration of library_items.

]

        25.a   Discussion:  Don't confuse these kinds of dependences with the
        run-time dependences among tasks and masters defined in 9.3, ``Task
        Dependence - Termination of Tasks''.

26   {semantic dependence (of one compilation unit upon another)} {dependence
(semantic)} A library_item depends semantically upon its parent declaration.
A subunit depends semantically upon its parent body.  A library_unit_body
depends semantically upon the corresponding library_unit_declaration, if any.

        26.a   Discussion:  The ``if any'' is necessary because library
        subprograms are not required to have a subprogram_declaration.

A compilation unit depends semantically upon each library_item mentioned in a
with_clause of the compilation unit.  In addition, if a given compilation
unit contains an attribute_reference of a type defined in another compilation
unit, then the given compilation unit depends semantically upon the other
compilation unit.  The semantic dependence relationship is transitive.

        26.b   To be honest:  If a given compilation unit contains a choice_
        parameter_specification, then the given compilation unit depends
        semantically upon the declaration of Ada.Exceptions.

        26.c   If a given compilation unit contains a pragma with an argument
        of a type defined in another compilation unit, then the given
        compilation unit depends semantically upon the other compilation
        unit.

        26.d   Discussion:  For example, a compilation unit containing
        X'Address depends semantically upon the declaration of package
        System.

        26.e   For the Address attribute, this fixes a hole in Ada 83.  Note
        that in almost all cases, the dependence will need to exist due to
        with_clauses, even without this rule.  Hence, the rule has very
        little effect on programmers.

        26.f   Note that the semantic dependence does not have the same
        effect as a with_clause; in order to denote a declaration in one of
        those packages, a with_clause will generally be needed.

        26.g   Note that no special rule is needed for an attribute_
        definition_clause, since an expression after use will require
        semantic dependence upon the compilation unit containing the type_
        declaration of interest.


     NOTES
27   (1) A simple program may consist of a single compilation unit.  A
     compilation need not have any compilation units; for example, its text
     can consist of pragmas.

   27.a   Ramification:  Such pragmas cannot have any arguments that are
        names, by a previous rule of this subclause.  A compilation can even
        be entirely empty, which is probably not useful.

   27.b   Some interesting properties of the three kinds of dependence:  The
        elaboration dependences also include the semantic dependences, except
        that subunits are taken together with their parents.  The semantic
        dependences partly determine the order in which the compilation units
        appear in the environment at compile time.  At run time, the order is
        partly determined by the elaboration dependences.

   27.c   The model whereby a child is inside its parent's declarative
        region, after the parent's declaration, as explained in 8.1, has the
        following ramifications:

         27.d  The restrictions on ``early'' use of a private type
               (RM83-7.4.1(4)) or a deferred constant (RM83-7.4.3(2)) do
               not apply to uses in child units, because they follow the
               full declaration.

         27.e  A library subprogram is never primitive, even if its
               profile includes a type declared immediately within the
               parent's package_specification, because the child is not
               declared immediately within the same package_specifica-
               tion as the type (so it doesn't declare a new primitive
               subprogram), and because the child is forbidden from
               overriding an old primitive subprogram.  It is
               immediately within the same declarative region, but not
               the same package_specification.  Thus, for a tagged type,
               it is not possible to call a child subprogram in a
               dispatching manner.  (This is also forbidden by the
               freezing rules.)  Similarly, it is not possible for the
               user to declare primitive subprograms of the types
               declared in the declaration of Standard, such as Integer
               (even if the rules were changed to allow a library unit
               whose name is an operator symbol).

         27.f  When the parent unit is ``used'' the simple names of the
               with'd child units are directly visible (see 8.4, ``Use
               Clauses'').

         27.g  When a parent body with's its own child, the defining
               name of the child is directly visible, and the parent
               body is not allowed to include a declaration of a
               homograph of the child unit immediately within the
               declarative_part of the body (RM83-8.3(17)).

   27.h   Note that ``declaration of a library unit'' is different from
        ``library_unit_declaration'' -- the former includes subprogram_body.
        Also, we sometimes really mean ``declaration of a view of a library
        unit'', which includes library_unit_renaming_declarations.
        {94-4625.a} {94-4626.a}

   27.i   The visibility rules generally imply that the renamed view of a
        library_unit_renaming_declaration has to be mentioned in a with_
        clause of the library_unit_renaming_declaration.

   27.j   To be honest:  The real rule is that the renamed library unit has
        to be visible in the library_unit_renaming_declaration.

   27.k   Reason:  In most cases, ``has to be visible'' means there has to be
        a with_clause.  However, it is possible in obscure cases to avoid the
        need for a with_clause; in particular, a compilation unit such as
        ``package P.Q renames P;'' is legal with no with_clauses (though not
        particularly interesting).  ASCII is physically nested in Standard,
        and so is not a library unit, and cannot be renamed as a library
        unit.

28   (2) The designator of a library function cannot be an operator_symbol,
     but a nonlibrary renaming_declaration is allowed to rename a library
     function as an operator.  Within a partition, two library subprograms
     are required to have distinct names and hence cannot overload each
     other.  {94-5002.a} However, renaming_declarations are allowed to define
     overloaded names for such subprograms, and a locally declared subprogram
     is allowed to overload a library subprogram.  The expanded name
     Standard.L can be used to denote a root library unit L (unless the
     declaration of Standard is hidden) since root library unit declarations
     occur immediately within the declarative region of package Standard.


                                  Examples

29   Examples of library units:

30  package Rational_Numbers.IO is  -- public child of Rational_Numbers, see 7.1
       procedure Put(R : in  Rational);
       procedure Get(R : out Rational);
    end Rational_Numbers.IO;

31  private procedure Rational_Numbers.Reduce(R : in out Rational);
                                    -- private child of Rational_Numbers

32  with Rational_Numbers.Reduce;   -- refer to a private child
    package body Rational_Numbers is
       ...
    end Rational_Numbers;

33  with Rational_Numbers.IO; use Rational_Numbers;
    with Ada.Text_io;               -- see A.10
    procedure Main is               -- a root library procedure
       R : Rational;
    begin
       R := 5/3;                    -- construct a rational number, see 7.1
       Ada.Text_IO.Put("The answer is: ");
       IO.Put(R);
       Ada.Text_IO.New_Line;
    end Main;

34  with Rational_Numbers.IO;
    package Rational_IO renames Rational_Numbers.IO;
                                    -- a library unit renaming declaration

35   Each of the above library_items can be submitted to the compiler
separately.

        35.a   Discussion:  Example of a generic package with children:

35.b        generic
               type Element is private;
               with function Image(E : Element) return String;
            package Generic_Bags is
               type Bag is limited private; -- A bag of Elements.
               procedure Add(B : in out Bag; E : Element);
               function Bag_Image(B : Bag) return String;
            private
               type Bag is ...;
            end Generic_Bags;

35.c        generic
            package Generic_Bags.Generic_Iterators is
               ... -- various additional operations on Bags.

35.d           generic
                  with procedure Use_Element(E : in Element);
                     -- Called once per bag element.
               procedure Iterate(B : in Bag);
            end Generic_Bags.Generic_Iterators;

        35.e   A package that instantiates the above generic units:

35.f        with Generic_Bags;
            with Generic_Bags.Generic_Iterators;
            package My_Abstraction is
                type My_Type is ...;
                function Image(X : My_Type) return String;
                package Bags_Of_My_Type is new Generic_Bags(My_Type, Image);
                package Iterators_Of_Bags_Of_My_Type is new Bags_Of_My_Type.Gen\
eric_Iterators;
            end My_Abstraction;

        35.g   In the above example, Bags_Of_My_Type has a nested generic
        unit called Generic_Iterators.  The second with_clause makes that
        nested unit visible.

        35.h   Here we show how the generic body could depend on one of its
        own children:

35.i        with Generic_Bags.Generic_Iterators;
            package body Generic_Bags is
               procedure Add(B : in out Bag; E : Element) is ... end Add;

35.j           package Iters is new Generic_Iterators;

35.k           function Bag_Image(B : Bag) return String is
                  Buffer : String(1..10_000);
                  Last : Integer := 0;

35.l              procedure Append_Image(E : in Element) is
                     Im : constant String := Image(E);
                  begin
                     if Last /= 0 then -- Insert a comma.
                        Last := Last + 1;
                        Buffer(Last) := ',';
                     end if;
                     Buffer(Last+1 .. Last+Im'Length) := Im;
                     Last := Last + Im'Length;
                  end Append_Image;

35.m              procedure Append_All is new Iters.Iterate(Append_Image);
               begin
                  Append_All(B);
                  return Buffer(1..Last);
               end Bag_Image;
            end Generic_Bags;

        {94-4933.a}


                            Extensions to Ada 83

        35.n   {extensions to Ada 83} The syntax rule for library_item is
        modified to allow the reserved word private before a library_unit_
        declaration.

        35.o   Children (other than children of Standard) are new in Ada 9X.

        35.p   Library unit renaming is new in Ada 9X.

                         Wording Changes From Ada 83

        35.q   Standard is considered a library unit in Ada 9X.  This
        simplifies the descriptions, since it implies that the parent of each
        library unit is a library unit.  (Standard itself has no parent, of
        course.)  As in Ada 83, the language does not define any way to
        recompile Standard, since the name given in the declaration of a
        library unit is always interpreted in relation to Standard.  That is,
        an attempt to compile a package Standard would result in
        Standard.Standard.



10.1.2 Context Clauses - With Clauses

1   [A context_clause is used to specify the library_items whose names are
needed within a compilation unit.]


                         Language Design Principles

        1.a   {one-pass context_clauses} The reader should be able to
        understand a context_clause without looking ahead.  Similarly, when
        compiling a context_clause, the compiler should not have to look
        ahead at subsequent context_items, nor at the compilation unit to
        which the context_clause is attached.  (We have not completely
        achieved this.)

                                   Syntax

2   context_clause ::= {context_item}

3   context_item ::= with_clause | use_clause

4   with_clause ::= with library_unit_name {, library_unit_name};


                            Name Resolution Rules

5   {scope (of a with_clause)} The scope of a with_clause that appears on a
library_unit_declaration or library_unit_renaming_declaration consists of the
entire declarative region of the declaration[, which includes all children
and subunits].  The scope of a with_clause that appears on a body consists of
the body[, which includes all subunits].

        5.a   Discussion:  Suppose a with_clause of a public library unit
        mentions one of its private siblings.  (This is only allowed on the
        body of the public library unit.)  We considered making the scope of
        that with_clause not include the visible part of the public library
        unit.  (This would only matter for a subprogram_body, since those are
        the only kinds of body that have a visible part, and only if the
        subprogram_body completes a subprogram_declaration, since otherwise
        the with_clause would be illegal.)  We did not put in such a rule for
        two reasons:  (1) It would complicate the wording of the rules,
        because we would have to split each with_clause into pieces, in order
        to correctly handle ``with P, Q;'' where P is public and Q is
        private.  (2) The conformance rules prevent any problems.  It doesn't
        matter if a type name in the spec of the body denotes the completion
        of a private_type_declaration.

        5.b   A with_clause also affects visibility within subsequent use_
        clauses and pragmas of the same context_clause, even though those are
        not in the scope of the with_clause.

6   {mentioned in a with_clause} {with_clause (mentioned in)} A library_item
is mentioned in a with_clause if it is denoted by a library_unit_name or a
prefix in the with_clause.

        6.a   Discussion:  With_clauses control the visibility of
        declarations or renamings of library units.  Mentioning a root
        library unit in a with_clause makes its declaration directly visible.
        Mentioning a non-root library unit makes its declaration visible.
        See Section 8 for details.

        6.b   Note that this rule implies that ``with A.B.C;'' is equivalent
        to ``with A, A.B, A.B.C;'' The reason for making a with_clause apply
        to all the ancestor units is to avoid ``visibility holes'' --
        situations in which an inner program unit is visible while an outer
        one is not.  Visibility holes would cause semantic complexity and
        implementation difficulty.

7   [Outside its own declarative region, the declaration or renaming of a
library unit can be visible only within the scope of a with_clause that
mentions it.  The visibility of the declaration or renaming of a library unit
otherwise follows from its placement in the environment.]


                               Legality Rules

8   If a with_clause of a given compilation_unit mentions a private child of
some library unit, then the given compilation_unit shall be either the
declaration of a private descendant of that library unit or the body or
subunit of a [(public or private)] descendant of that library unit.

        8.a   Reason:  The purpose of this rule is to prevent a private child
        from being visible (or even semantically depended-on) from outside
        the subsystem rooted at its parent.

        8.b   Discussion:  This rule violates the one-pass context_clauses
        Language Design Principle.  We rationalize this by saying that at
        least that Language Design Principle works for legal compilation
        units.

        8.c   Example:

8.d         package A is
            end A;

8.e         package A.B is
            end A.B;

8.f         private package A.B.C is
            end A.B.C;

8.g         package A.B.C.D is
            end A.B.C.D;

8.h         with A.B.C; -- (1)
            private package A.B.X is
            end A.B.X;

8.i         package A.B.Y is
            end A.B.Y;

8.j         with A.B.C; -- (2)
            package body A.B.Y is
            end A.B.Y;

        8.k   (1) is OK because it's a private child of A.B -- it would be
        illegal if we made A.B.X a public child of A.B.  (2) is OK because
        it's the body of a child of A.B.  It would be illegal to say ``with
        A.B.C;'' on any library_item whose name does not start with ``A.B''.
        Note that mentioning A.B.C.D in a with_clause automatically mentions
        A.B.C as well, so ``with A.B.C.D;'' is illegal in the same places as
        ``with A.B.C;''.

        8.l   To be honest:  For the purposes of this rule, if a subprogram_
        body has no preceding subprogram_declaration, the subprogram_body
        should be considered a declaration and not a body.  Thus, it is
        illegal for such a subprogram_body to mention one of its siblings in
        a with_clause if the sibling is a private library unit.  {94-4625.a}
        {94-4626.a}


     NOTES
9    (3) A library_item mentioned in a with_clause of a compilation unit is
     visible within the compilation unit and hence acts just like an ordinary
     declaration.  Thus, within a compilation unit that mentions its
     declaration, the name of a library package can be given in use_clauses
     and can be used to form expanded names, a library subprogram can be
     called, and instances of a generic library unit can be declared.  If a
     child of a parent generic package is mentioned in a with_clause, then
     the corresponding declaration nested within each visible instance is
     visible within the compilation unit.  {94-4933.a}

   9.a   Ramification:  The rules given for with_clauses are such that the
        same effect is obtained whether the name of a library unit is
        mentioned once or more than once by the applicable with_clauses, or
        even within a given with_clause.

   9.b   If a with_clause mentions a library_unit_renaming_declaration, it
        only ``mentions'' the prefixes appearing explicitly in the with_
        clause (and the renamed view itself); the with_clause is not defined
        to mention the ancestors of the renamed entity.  Thus, if X renames
        Y.Z, then ``with X;'' does not make the declarations of Y or Z
        visible.  Note that this does not cause the dreaded visibility holes
        mentioned above.


                            Extensions to Ada 83

        9.c   {extensions to Ada 83} The syntax rule for with_clause is
        modified to allow expanded name notation.

        9.d   A use_clause in a context_clause may be for a package (or type)
        nested in a library package.

                         Wording Changes From Ada 83

        9.e   The syntax rule for context_clause is modified to more closely
        reflect the semantics.  The Ada 83 syntax rule implies that the use_
        clauses that appear immediately after a particular with_clause are
        somehow attached to that with_clause, which is not true.  The new
        syntax allows a use_clause to appear first, but that is prevented by
        a textual rule that already exists in Ada 83.

        9.f   The concept of ``scope of a with_clause'' (which is a region of
        text) replaces RM83's notion of ``apply to'' (a with_clause applies
        to a library_item) The visibility rules are interested in a region of
        text, not in a set of compilation units.

        9.g   No need to define ``apply to'' for use_clauses.  Their
        semantics are fully covered by the ``scope (of a use_clause)''
        definition in 8.4.



10.1.3 Subunits of Compilation Units

1   [Subunits are like child units, with these (important) differences:
subunits support the separate compilation of bodies only (not declarations);
the parent contains a body_stub to indicate the existence and place of each
of its subunits; declarations appearing in the parent's body can be visible
within the subunits.]


                                   Syntax

2   body_stub ::= subprogram_body_stub | package_body_stub | task_body_stub | p\
rotected_body_stub

3   subprogram_body_stub ::= subprogram_specification is separate;

        3.a   Discussion:  Although this syntax allows a parent_unit_name,
        that is disallowed by 10.1.1, ``Compilation Units - Library Units''.

4   package_body_stub ::= package body defining_identifier is separate;

5   task_body_stub ::= task body defining_identifier is separate;

6   protected_body_stub ::= protected body defining_identifier is separate;

7   subunit ::= separate (parent_unit_name) proper_body


                               Legality Rules

8   {parent body (of a subunit)} The parent body of a subunit is the body of
the program unit denoted by its parent_unit_name.  {subunit} The term subunit
is used to refer to a subunit and also to the proper_body of a subunit.
{94-4768.b}

9   The parent body of a subunit shall be present in the current environment,
and shall contain a corresponding body_stub with the same defining_identifier
as the subunit.

        9.a   Discussion:  This can't be a Name Resolution Rule, because a
        subunit is not a complete context.

10   A package_body_stub shall be the completion of a package_declaration or
generic_package_declaration; a task_body_stub shall be the completion of a
task_declaration; a protected_body_stub shall be the completion of a
protected_declaration.

11   In contrast, a subprogram_body_stub need not be the completion of a
previous declaration, [in which case the _stub declares the subprogram].  If
the _stub is a completion, it shall be the completion of a subprogram_
declaration or generic_subprogram_declaration.  The profile of a subprogram_
body_stub that completes a declaration shall conform fully to that of the
declaration.  {full conformance (required)}

        11.a   Discussion:  The part about subprogram_body_stubs echoes the
        corresponding rule for subprogram_bodies in 6.3, ``Subprogram
        Bodies''.

12   A subunit that corresponds to a body_stub shall be of the same kind
(package_, subprogram_, task_, or protected_) as the body_stub.  The profile
of a subprogram_body subunit shall be fully conformant to that of the
corresponding body_stub.  {full conformance (required)}

13   A body_stub shall appear immediately within the declarative_part of a
compilation unit body.  This rule does not apply within an instance of a
generic unit.

        13.a   Discussion:  {methodological restriction} This is a
        methodological restriction; that is, it is not necessary for the
        semantics of the language to make sense.

14   The defining_identifiers of all body_stubs that appear immediately
within a particular declarative_part shall be distinct.


                           Post-Compilation Rules

15   {post-compilation rules} For each body_stub, there shall be a subunit
containing the corresponding proper_body.


     NOTES
16   (4) The rules in 10.1.4, ``The Compilation Process'' say that a body_
     stub is equivalent to the corresponding proper_body.  This implies:

        17  Visibility within a subunit is the visibility that would be
            obtained at the place of the corresponding body_stub (within
            the parent body) if the context_clause of the subunit were
            appended to that of the parent body.

 17.a   Ramification:  Recursively.  Note that this transformation might
        make the parent illegal; hence it is not a true equivalence, but
        applies only to visibility within the subunit.

        18  The effect of the elaboration of a body_stub is to elaborate
            the subunit.

 18.a   Ramification:  The elaboration of a subunit is part of its
        parent body's elaboration, whereas the elaboration of a child
        unit is not part of its parent declaration's elaboration.

   18.b   Ramification:  A library_item that is mentioned in a with_clause of
        a subunit can be hidden (from direct visiblity) by a declaration
        (with the same identifier) given in the subunit.  Moreover, such a
        library_item can even be hidden by a declaration given within the
        parent body since a library unit is declared in its parent's
        declarative region; this however does not affect the interpretation
        of the with_clauses themselves, since only library_items are visible
        or directly visible in with_clauses.

   18.c   The body of a protected operation cannot be a subunit.  This
        follows from the syntax rules.  The body of a protected unit can be a
        subunit.


                                  Examples

19   The package Parent is first written without subunits:

20  package Parent is
        procedure Inner;
    end Parent;

21  with Ada.Text_IO;
    package body Parent is
        Variable : String := "Hello, there.";
        procedure Inner is
        begin
            Ada.Text_IO.Put_Line(Variable);
        end Inner;
    end Parent;

22   The body of procedure Inner may be turned into a subunit by rewriting
the package body as follows (with the declaration of Parent remaining the
same):

23  package body Parent is
        Variable : String := "Hello, there.";
        procedure Inner is separate;
    end Parent;

24  with Ada.Text_IO;
    separate(Parent)
    procedure Inner is
    begin
        Ada.Text_IO.Put_Line(Variable);
    end Inner;


                            Extensions to Ada 83

        24.a   {extensions to Ada 83} Subunits of the same ancestor library
        unit are no longer restricted to have distinct identifiers.  Instead,
        we require only that the full expanded names be distinct.



10.1.4 The Compilation Process

1   {environment} {environment declarative_part} Each compilation unit
submitted to the compiler is compiled in the context of an environment
declarative_part (or simply, an environment), which is a conceptual
declarative_part that forms the outermost declarative region of the context
of any compilation.  At run time, an environment forms the declarative_part
of the body of the environment task of a partition (see 10.2, ``Program
Execution'').

        1.a   Ramification:  At compile time, there is no particular
        construct that the declarative region is considered to be nested
        within -- the environment is the universe.

        1.b   To be honest:  The environment is really just a portion of a
        declarative_part, since there might, for example, be bodies that do
        not yet exist.

2   The declarative_items of the environment are library_items appearing in
an order such that there are no forward semantic dependences.  Each included
subunit occurs in place of the corresponding stub.  The visibility rules
apply as if the environment were the outermost declarative region, except
that with_clauses are needed to make declarations of library units visible
(see 10.1.2).

3   The mechanisms for creating an environment and for adding and replacing
compilation units within an environment are implementation defined.

        3.a   Implementation defined:  The mechanisms for creating an
        environment and for adding and replacing compilation units.

        3.b   Ramification:  The traditional model, used by most Ada 83
        implementations, is that one places a compilation unit in the
        environment by compiling it.  Other models are possible.  For
        example, an implementation might define the environment to be a
        directory; that is, the compilation units in the environment are all
        the compilation units in the source files contained in the directory.
        In this model, the mechanism for replacing a compilation unit with a
        new one is simply to edit the source file containing that compilation
        unit.


                            Name Resolution Rules

4   If a library_unit_body that is a subprogram_body is submitted to the
compiler, it is interpreted only as a completion if a library_unit_
declaration for a subprogram or a generic subprogram with the same defining_
program_unit_name already exists in the environment (even if the profile of
the body is not type conformant with that of the declaration); otherwise the
subprogram_body is interpreted as both the declaration and body of a library
subprogram.  {type conformance [partial]}

        4.a   Ramification:  The principle here is that a subprogram_body
        should be interpreted as only a completion if and only if it
        ``might'' be legal as the completion of some preexisting declaration,
        where ``might'' is defined in a way that does not require overload
        resolution to determine.

        4.b   Hence, if the preexisting declaration is a subprogram_
        declaration or generic_subprogram_declaration, we treat the new
        subprogram_body as its completion, because it ``might'' be legal.  If
        it turns out that the profiles don't fully conform, it's an error.
        In all other cases (the preexisting declaration is a package or a
        generic package, or an instance of a generic subprogram, or a
        renaming, or a ``spec-less'' subprogram, or in the case where there
        is no preexisting thing), the subprogram_body declares a new
        subprogram.

        4.c   See also AI-00266/09.


                               Legality Rules

5   When a compilation unit is compiled, all compilation units upon which it
depends semantically shall already exist in the environment; {consistency
(among compilation units)} the set of these compilation units shall be
consistent in the sense that the new compilation unit shall not semantically
depend (directly or indirectly) on two different versions of the same
compilation unit, nor on an earlier version of itself.

        5.a   Discussion:  For example, if package declarations A and B both
        say ``with X;'', and the user compiles a compilation unit that says
        ``with A, B;'', then the A and B have to be talking about the same
        version of X.

        5.b   Ramification:  What it means to be a ``different version'' is
        not specified by the language.  In some implementations, it means
        that the compilation unit has been recompiled.  In others, it means
        that the source of the compilation unit has been edited in some
        significant way.

        5.c   Note that an implementation cannot require the existence of
        compilation units upon which the given one does not semantically
        depend.  For example, an implementation is required to be able to
        compile a compilation unit that says "with A;" when A's body does not
        exist.  It has to be able to detect errors without looking at A's
        body.

        5.d   Similarly, the implementation has to be able to compile a call
        to a subprogram for which a pragma Inline has been specified without
        seeing the body of that subprogram -- inlining would not be achieved
        in this case, but the call is still legal.


                         Implementation Permissions

6   The implementation may require that a compilation unit be legal before
inserting it into the environment.

7   When a compilation unit that declares or renames a library unit is added
to the environment, the implementation may remove from the environment any
preexisting library_item with the same defining_program_unit_name.  When a
compilation unit that is a subunit or the body of a library unit is added to
the environment, the implementation may remove from the environment any
preexisting version of the same compilation unit.  When a given compilation
unit is removed from the environment, the implementation may also remove any
compilation unit that depends semantically upon the given one.  If the given
compilation unit contains the body of a subprogram to which a pragma Inline
applies, the implementation may also remove any compilation unit containing a
call to that subprogram.

        7.a   Ramification:  The permissions given in this paragraph
        correspond to the traditional model, where compilation units enter
        the environment by being compiled into it, and the compiler checks
        their legality at that time.  A implementation model in which the
        environment consists of all source files in a given directory might
        not want to take advantage of these permissions.  Compilation units
        would not be checked for legality as soon as they enter the
        environment; legality checking would happen later, when compilation
        units are compiled.  In this model, compilation units might never be
        automatically removed from the environment; they would be removed
        when the user explicitly deletes a source file.

        7.b   Note that the rule is recursive: if the above permission is
        used to remove a compilation unit containing an inlined subprogram
        call, then compilation units that depend semantically upon the
        removed one may also be removed, and so on.

        7.c   Note that here we are talking about dependences among existing
        compilation units in the environment; it doesn't matter what with_
        clauses are attached to the new compilation unit that triggered all
        this.

        7.d   An implementation may have other modes in which compilation
        units in addition to the ones mentioned above are removed.  For
        example, an implementation might inline subprogram calls without an
        explicit pragma Inline.  If so, it either has to have a mode in which
        that optimization is turned off, or it has to automatically
        regenerate code for the inlined calls without requiring the user to
        resubmit them to the compiler.


     NOTES
8    (5) The rules of the language are enforced across compilation and
     compilation unit boundaries, just as they are enforced within a single
     compilation unit.

   8.a   Ramification:  Note that Section 1 requires an implementation to
        detect illegal compilation units at compile time.

9    (6) {library} An implementation may support a concept of a library,
     which contains library_items.  If multiple libraries are supported, the
     implementation has to define how a single environment is constructed
     when a compilation unit is submitted to the compiler.  Naming conflicts
     between different libraries might be resolved by treating each library
     as the root of a hierarchy of child library units.  {program library:
     see library}

   9.a   Implementation Note:  Alternatively, naming conflicts could be
        resolved via some sort of hiding rule.

   9.b   Discussion:  For example, the implementation might support a command
        to import library Y into library X. If a root library unit called LU
        (that is, Standard.LU) exists in Y, then from the point of view of
        library X, it could be called Y.LU.  X might contain library units
        that say, ``with Y.LU;''.

10   (7) A compilation unit containing an instantiation of a separately
     compiled generic unit does not semantically depend on the body of the
     generic unit.  Therefore, replacing the generic body in the environment
     does not result in the removal of the compilation unit containing the
     instantiation.

   10.a   Implementation Note:  Therefore, implementations have to be
        prepared to automatically instantiate generic bodies at link-time, as
        needed.  This might imply a complete automatic recompilation, but it
        is the intent of the language that generic bodies can be
        (re)instantiated without forcing all of the compilation units that
        semantically depend on the compilation unit containing the
        instantiation to be recompiled.



10.1.5 Pragmas and Program Units

1   [This subclause discusses pragmas related to program units, library
units, and compilations.]


                            Name Resolution Rules

2   {program unit pragma [distributed]} {pragma, program unit [distributed]}
Certain pragmas are defined to be program unit pragmas.  {apply [to a program
unit by a program unit pragma]} A name given as the argument of a program
unit pragma shall resolve to denote the declarations or renamings of one or
more program units that occur immediately within the declarative region or
compilation in which the pragma immediately occurs, or it shall resolve to
denote the declaration of the immediately enclosing program unit (if any);
the pragma applies to the denoted program unit(s).  If there are no names
given as arguments, the pragma applies to the immediately enclosing program
unit.  {94-4973.a}

        2.a   Ramification:  The fact that this is a Name Resolution Rule
        means that the pragma will not apply to declarations from outer
        declarative regions.


                               Legality Rules

3   A program unit pragma shall appear in one of these places:

    4  At the place of a compilation_unit, in which case the pragma
       shall immediately follow in the same compilation (except for
       other pragmas) a library_unit_declaration that is a subprogram_
       declaration, generic_subprogram_declaration, or generic_instan-
       tiation, and the pragma shall have an argument that is a name
       denoting that declaration.

 4.a    Ramification:  The name has to denote the immediately preceding
        library_unit_declaration.

    5  Immediately within the declaration of a program unit and before
       any nested declaration, in which case the argument, if any, shall
       be a direct_name that denotes the immediately enclosing program
       unit declaration.

 5.a    Ramification:  The argument is optional in this case.

    6  At the place of a declaration other than the first, of a
       declarative_part or program unit declaration, in which case the
       pragma shall have an argument, which shall be a direct_name that
       denotes one or more of the following (and nothing else):  a
       subprogram_declaration, a generic_subprogram_declaration, or a
       generic_instantiation, of the same declarative_part or program
       unit declaration.

 6.a    Ramification:  If you want to denote a subprogram_body that is
        not a completion, or a package_declaration, for example, you
        have to put the pragma inside.

7   {library unit pragma [distributed]} {pragma, library unit [distributed]}
{program unit pragma [library unit pragmas]} {pragma, program unit [library
unit pragmas]} Certain program unit pragmas are defined to be library unit
pragmas.  The name, if any, in a library unit pragma shall denote the
declaration of a library unit.

        7.a   Ramification:  This, together with the rules for program unit
        pragmas above, implies that if a library unit pragma applies to a
        subprogram_declaration (and similar things), it has to appear
        immediately after the compilation_unit, whereas if the pragma applies
        to a package_declaration, a subprogram_body that is not a completion
        (and similar things), it has to appear inside, as the first
        declarative_item.


                           Post-Compilation Rules

8   {post-compilation rules} {configuration pragma [distributed]} {pragma,
configuration [distributed]} Certain pragmas are defined to be configuration
pragmas; they shall appear before the first compilation_unit of a
compilation.  [They are generally used to select a partition-wide or
system-wide option.]  The pragma applies to all compilation_units appearing
in the compilation, unless there are none, in which case it applies to all
future compilation_units compiled into the same environment.


                         Implementation Permissions

9   An implementation may place restrictions on configuration pragmas, so
long as it allows them when the environment contains no library_items other
than those of the predefined environment.



10.1.6 Environment-Level Visibility Rules

1   [The normal visibility rules do not apply within a parent_unit_name or a
context_clause, nor within a pragma that appears at the place of a
compilation unit.  The special visibility rules for those contexts are given
here.]
                              Static Semantics

2   {directly visible [within the parent_unit_name of a library unit]}
{visible [within the parent_unit_name of a library unit]} {directly visible
[within a with_clause]} {visible [within a with_clause]} Within the parent_
unit_name at the beginning of a library_item, and within a with_clause, the
only declarations that are visible are those that are library_items of the
environment, and the only declarations that are directly visible are those
that are root library_items of the environment.  {notwithstanding}
Notwithstanding the rules of 4.1.3, an expanded name in a with_clause may
consist of a prefix that denotes a generic package and a selector_name that
denotes a child of that generic package.  [(The child is necessarily a
generic unit; see 10.1.1.)]  {94-4933.a}

        2.a   Ramification:  In ``package P.Q.R is ... end P.Q.R;'', this
        rule requires P to be a root library unit, and Q to be a library unit
        (because those are the things that are directly visible and visible).
        Note that visibility does not apply between the ``end'' and the
        ``;''.

        2.b   Physically nested declarations are not visible at these places.

        2.c   Reason:  Although Standard is visible at these places, it is
        impossible to name it, since it is not directly visible, and it has
        no parent.

        2.d   Reason:  The ``notwithstanding'' part allows ``with A.B;''
        where A is a generic library package and B is one of its (generic)
        children.  This is necessary because it is not normally legal to use
        an expanded name to reach inside a generic package.

3   {directly visible [within a use_clause in a context_clause]} {visible
[within a use_clause in a context_clause]} {directly visible [within a pragma
in a context_clause]} {visible [within a pragma in a context_clause]} Within
a use_clause or pragma that is within a context_clause, each library_item
mentioned in a previous with_clause of the same context_clause is visible,
and each root library_item so mentioned is directly visible.  In addition,
within such a use_clause, if a given declaration is visible or directly
visible, each declaration that occurs immediately within the given
declaration's visible part is also visible.  No other declarations are
visible or directly visible.

        3.a   Discussion:  Note the word ``same''.  For example, if a with_
        clause on a declaration mentions X, this does not make X visible in
        use_clauses and pragmas that are on the body.  The reason for this
        rule is the one-pass context_clauses Language Design Principle.

        3.b   Note that the second part of the rule does not mention pragmas.

4   {directly visible [within the parent_unit_name of a subunit]} {visible
[within the parent_unit_name of a subunit]} Within the parent_unit_name of a
subunit, library_items are visible as they are in the parent_unit_name of a
library_item; in addition, the declaration corresponding to each body_stub in
the environment is also visible.

        4.a   Ramification:  For a subprogram without a separate subprogram_
        declaration, the body_stub itself is the declaration.

5   {directly visible [within a pragma that appears at the place of a
compilation unit]} {visible [within a pragma that appears at the place of a
compilation unit]} Within a pragma that appears at the place of a compilation
unit, the immediately preceding library_item and each of its ancestors is
visible.  The ancestor root library_item is directly visible.


                         Wording Changes From Ada 83

        5.a   The special visibility rules that apply within a parent_unit_
        name or a context_clause, and within a pragma that appears at the
        place of a compilation_unit are clarified.

        5.b   Note that a context_clause is not part of any declarative
        region.

        5.c   We considered making the visibility rules within parent_unit_
        names and context_clauses follow from the context of compilation.
        However, this attempt failed for various reasons.  For example, it
        would require use_clauses in context_clauses to be within the
        declarative region of Standard, which sounds suspiciously like a
        kludge.  And we would still need a special rule to prevent seeing
        things (in our own context_clause) that were with-ed by our parent,
        etc.
10.2 Program Execution

1   {program} {program execution} {running a program: see program execution}
An Ada program consists of a set of partitions[, which can execute in
parallel with one another, possibly in a separate address space, and possibly
on a separate computer.]


                           Post-Compilation Rules

2   {post-compilation rules} {partition [distributed]} {partition building} A
partition is a program or part of a program that can be invoked from outside
the Ada implementation.  [For example, on many systems, a partition might be
an executable file generated by the system linker.]  {explicitly assign} The
user can explicitly assign library units to a partition.  The assignment is
done in an implementation-defined manner.  The compilation units included in
a partition are those of the explicitly assigned library units, as well as
other compilation units needed by those library units.  The compilation units
needed by a given compilation unit are determined as follows (unless
specified otherwise via an implementation-defined pragma, or by some other
implementation-defined means):  {linking: see partition building}
{compilation units needed (by a compilation unit) [distributed]} {needed (of
a compilation unit by another) [distributed]}

        2.a   Discussion:  From a run-time point of view, an Ada 9X partition
        is identical to an Ada 83 program -- implementations were always
        allowed to provide inter-program communication mechanisms.  The
        additional semantics of partitions is that interfaces between them
        can be defined to obey normal language rules (as is done in Annex E,
        ``Distributed Systems''), whereas interfaces between separate
        programs had no particular semantics.

        2.b   Implementation defined:  The manner of explicitly assigning
        library units to a partition.

        2.c   Implementation defined:  The implementation-defined means, if
        any, of specifying which compilation units are needed by a given
        compilation unit.

        2.d   Discussion:  There are no pragmas that ``specify otherwise''
        defined by the core language.  However, an implementation is allowed
        to provide such pragmas, and in fact Annex E, ``Distributed Systems''
        defines some pragmas whose semantics includes reducing the set of
        compilation units described here.

    3  A compilation unit needs itself;

    4  If a compilation unit is needed, then so are any compilation
       units upon which it depends semantically;

    5  If a library_unit_declaration is needed, then so is any
       corresponding library_unit_body;

    6  If a compilation unit with stubs is needed, then so are any
       corresponding subunits.

 6.a    Discussion:  Note that in the environment, the stubs are
        replaced with the corresponding proper_bodies.

        6.b   Discussion:  Note that a child unit is not included just
        because its parent is included -- to include a child, mention it in a
        with_clause.

7   {main subprogram (for a partition)} The user can optionally designate (in
an implementation-defined manner) one subprogram as the main subprogram for
the partition.  A main subprogram, if specified, shall be a subprogram.

        7.a   Discussion:  This may seem superfluous, since it follows from
        the definition.  But we would like to have every error message that
        might be generated (before run time) by an implementation correspond
        to some explicitly stated ``shall'' rule.

        7.b   Of course, this does not mean that the ``shall'' rules
        correspond one-to-one with an implementation's error messages.  For
        example, the rule that says overload resolution ``shall'' succeed in
        producing a single interpretation would correspond to many error
        messages in a good implementation -- the implementation would want to
        explain to the user exactly why overload resolution failed.  This is
        especially true for the syntax rules -- they are considered part of
        overload resolution, but in most cases, one would expect an error
        message based on the particular syntax rule that was violated.

        7.c   Implementation defined:  The manner of designating the main
        subprogram of a partition.

        7.d   Ramification:  An implementation cannot require the user to
        specify, say, all of the library units to be included.  It has to
        support, for example, perhaps the most typical case, where the user
        specifies just one library unit, the main program.  The
        implementation has to do the work of tracking down all the other
        ones.

8   {environment task} Each partition has an anonymous environment task[,
which is an implicit outermost task whose execution elaborates the library_
items of the environment declarative_part, and then calls the main
subprogram, if there is one.  A partition's execution is that of its tasks.]

        8.a   Ramification:  An environment task has no master; all
        nonenvironment tasks have masters.

        8.b   An implementation is allowed to support multiple concurrent
        executions of the same partition.

9   [The order of elaboration of library units is determined primarily by the
elaboration dependences.]  {elaboration dependence (library_item on another)}
{dependence (elaboration)} There is an elaboration dependence of a given
library_item upon another if the given library_item or any of its subunits
depends semantically on the other library_item.  In addition, if a given
library_item or any of its subunits has a pragma Elaborate or Elaborate_All
that mentions another library unit, then there is an elaboration dependence
of the given library_item upon the body of the other library unit, and, for
Elaborate_All only, upon each library_item needed by the declaration of the
other library unit.

        9.a   Discussion:  See above for a definition of which library_items
        are ``needed by'' a given declaration.

        9.b   Note that elaboration dependences are among library_items,
        whereas the other two forms of dependence are among compilation
        units.  Note that elaboration dependence includes semantic
        dependence.  It's a little bit sad that pragma Elaborate_Body can't
        be folded into this mechanism.  It follows from the definition that
        the elaboration dependence relationship is transitive.  Note that the
        wording of the rule does not need to take into account a semantic
        dependence of a library_item or one of its subunits upon a subunit of
        a different library unit, because that can never happen.

10   The environment task for a partition has the following structure:

11  task Environment_Task;

12  task body Environment_Task is
        ... (1) -- The environment declarative_part
                -- (that is, the sequence of library_items) goes here.
    begin
        ... (2) -- Call the main subprogram, if there is one.
    end Environment_Task;

        12.a   Ramification:  The name of the environment task is written in
        italics here to indicate that this task is anonymous.

        12.b   Discussion:  The model is different for a ``passive
        partition'' (see E.1).  Either there is no environment task, or its
        sequence_of_statements is an infinite loop rather than a call on a
        main subprogram.

13   {environment declarative_part [for the environment task of a partition]}
The environment declarative_part at (1) is a sequence of declarative_items
consisting of copies of the library_items included in the partition.  [The
order of elaboration of library_items is the order in which they appear in
the environment declarative_part]:

   14  The order of all included library_items is such that there are no
       forward elaboration dependences.

 14.a   Ramification:  This rule is written so that if a library_item
        depends on itself, we don't require it to be elaborated before
        itself.  See AI-00113/12.  This can happen only in pathological
        circumstances.  For example, if a library subprogram_body has no
        corresponding subprogram_declaration, and one of the subunits of
        the subprogram_body mentions the subprogram_body in a with_
        clause, the subprogram_body will depend on itself.  For another
        example, if a library_unit_body applies a pragma Elaborate_All
        to its own declaration, then the library_unit_body will depend
        on itself.

   15  Any included library_unit_declaration to which a pragma
       Elaborate_Body applies is immediately followed by its library_
       unit_body, if included.

 15.a   Discussion:  This implies that the body of such a library unit
        shall not ``with'' any of its own children, or anything else
        that depends semantically upon the declaration of the library
        unit.

   16  All library_items declared pure occur before any that are not
       declared pure.

   17  All preelaborated library_items occur before any that are not
       preelaborated.

        17.a   Discussion:  Normally, if two partitions contain the same
        compilation unit, they each contain a separate copy of that
        compilation unit.  See Annex E, ``Distributed Systems'' for cases
        where two partitions share the same copy of something.

        17.b   There is no requirement that the main subprogram be elaborated
        last.  In fact, it is possible to write a partition in which the main
        subprogram cannot be elaborated last.

        17.c   Ramification:  This declarative_part has the properties
        required of all environments (see 10.1.4).  However, the environment
        declarative_part of a partition will typically contain fewer
        compilation units than the environment declarative_part used at
        compile time -- only the ``needed'' ones are included in the
        partition.

18   There shall be a total order of the library_items that obeys the above
rules.  The order is otherwise implementation defined.
        18.a   Discussion:  The only way to violate this rule is to have
        Elaborate, Elaborate_All, or Elaborate_Body pragmas that cause
        circular ordering requirements, thus preventing an order that has no
        forward elaboration dependences.

        18.b   Implementation defined:  The order of elaboration of library_
        items.

        18.c   To be honest:  {requires a completion [library_unit_
        declaration]} {notwithstanding} Notwithstanding what the RM9X says
        elsewhere, each rule that requires a declaration to have a
        corresponding completion is considered to be a Post-Compilation Rule
        when the declaration is that of a library unit.

        18.d   Discussion:  Such rules may be checked at ``link time,'' for
        example.  Rules requiring the completion to have certain properties,
        on the other hand, are checked at compile time of the completion.

19   The full expanded names of the library units and subunits included in a
given partition shall be distinct.  {94-4599.c} {94-4577.a} {94-4460.a}
{94-4461.a} {94-4753.a}

        19.a   Reason:  This is a Post-Compilation Rule because making it a
        Legality Rule would violate the Language Design Principle labeled
        ``legality determinable via semantic dependences.''

20   The sequence_of_statements of the environment task (see (2) above)
consists of either:

   21  A call to the main subprogram, if the partition has one.  If the
       main subprogram has parameters, they are passed; where the
       actuals come from is implementation defined.  What happens to the
       result of a main function is also implementation defined.

 21.a   Implementation defined:  Parameter passing and function return
        for the main subprogram.

22   or:

   23  A null_statement, if there is no main subprogram.

 23.a   Discussion:  For a passive partition, either there is no
        environment task, or its sequence_of_statements is an infinite
        loop.  See E.1.

24   The mechanisms for building and running partitions are implementation
defined.  [These might be combined into one operation, as, for example, in
dynamic linking, or ``load-and-go'' systems.]

        24.a   Implementation defined:  The mechanisms for building and
        running partitions.


                              Dynamic Semantics

25   {execution [program]} The execution of a program consists of the
execution of a set of partitions.  Further details are implementation
defined.  {execution [partition]} The execution of a partition starts with
the execution of its environment task, ends when the environment task
terminates, and includes the executions of all tasks of the partition.  [The
execution of the (implicit) task_body of the environment task acts as a
master for all other tasks created as part of the execution of the partition.
When the environment task completes (normally or abnormally), it waits for
the termination of all such tasks, and then finalizes any remaining objects
of the partition.]

        25.a   Ramification:  The ``further details'' mentioned above
        include, for example, program termination -- it is implementation
        defined.  There is no need to define it here; it's entirely up to the
        implementation whether it wants to consider the program as a whole to
        exist beyond the existence of individual partitions.

        25.b   Implementation defined:  The details of program execution,
        including program termination.

        25.c   To be honest:  {termination [of a partition]} {normal
        termination [of a partition]} {termination [normal]} {abnormal
        termination [of a partition]} {termination [abnormal]} The execution
        of the partition terminates (normally or abnormally) when the
        environment task terminates (normally or abnormally, respectively).


                          Bounded (Run-Time) Errors

26   {bounded error} {Program_Error (raised by failure of run-time check)}
Once the environment task has awaited the termination of all other tasks of
the partition, any further attempt to create a task (during finalization) is
a bounded error, and may result in the raising of Program_Error either upon
creation or activation of the task.  {unspecified [partial]} If such a task
is activated, it is not specified whether the task is awaited prior to
termination of the environment task.


                         Implementation Requirements

27   The implementation shall ensure that all compilation units included in a
partition are consistent with one another, and are legal according to the
rules of the language.

        27.a   Discussion:  The consistency requirement implies that a
        partition cannot contain two versions of the same compilation unit.
        That is, a partition cannot contain two different library units with
        the same full expanded name, nor two different bodies for the same
        program unit.  For example, suppose we compile the following:

27.b        package A is -- Version 1.
                ...
            end A;

27.c        with A;
            package B is
            end B;

27.d        package A is -- Version 2.
                ...
            end A;

27.e        with A;
            package C is
            end C;

        27.f   It would be wrong for a partition containing B and C to
        contain both versions of A. Typically, the implementation would
        require the use of Version 2 of A, which might require the
        recompilation of B. Alternatively, the implementation might
        automatically recompile B when the partition is built.  A third
        alternative would be an incremental compiler that, when Version 2 of
        A is compiled, automatically patches the object code for B to reflect
        the changes to A (if there are any relevant changes -- there might
        not be any).

        27.g   An implementation that supported fancy version management
        might allow the use of Version 1 in some circumstances.  In no case
        can the implementation allow the use of both versions in the same
        partition (unless, of course, it can prove that the two versions are
        semantically identical).

        27.h   The core language says nothing about inter-partition
        consistency; see also Annex E, ``Distributed Systems''.


                         Implementation Permissions

28   {active partition} The kind of partition described in this clause is
known as an active partition.  An implementation is allowed to support other
kinds of partitions, with implementation-defined semantics.

        28.a   Implementation defined:  The semantics of any nonactive
        partitions supported by the implementation.

        28.b   Discussion:  Annex E, ``Distributed Systems'' defines the
        concept of passive partitions; they may be thought of as a partition
        without an environment task, or as one with a particularly simple
        form of environment task, having an infinite loop rather than a call
        on a main subprogram as its sequence_of_statements.

29   An implementation may restrict the kinds of subprograms it supports as
main subprograms.  However, an implementation is required to support all main
subprograms that are public parameterless library procedures.

        29.a   Ramification:  The implementation is required to support main
        subprograms that are procedures declared by generic_instantiations,
        as well as those that are children of library units other than
        Standard.  {94-4908.a} Generic units are, of course, not allowed to
        be main subprograms, since they are not subprograms.

        29.b   Note that renamings are irrelevant to this rule.  This rules
        says which subprograms (not views) have to be supported.  The
        implementation can choose any way it wants for the user to indicate
        which subprogram should be the main subprogram.  An implementation
        might allow any name of any view, including those declared by
        renamings.  Another implementation might require it to be the
        original name.  Another implementation still might use the name of
        the source file or some such thing.

30   If the environment task completes abnormally, the implementation may
abort any dependent tasks.

        30.a   Reason:  If the implementation does not take advantage of this
        permission, the normal action takes place -- the environment task
        awaits those tasks.

        30.b   The possibility of aborting them is not shown in the
        Environment_Task code above, because there is nowhere to put an
        exception_handler that can handle exceptions raised in both the
        environment declarative_part and the main subprogram, such that the
        dependent tasks can be aborted.  If we put an exception_handler in
        the body of the environment task, then it won't handle exceptions
        that occur during elaboration of the environment declarative_part.
        If we were to move those things into a nested block_statement, with
        the exception_handler outside that, then the block_statement would
        await the library tasks we are trying to abort.

        30.c   Furthermore, this is merely a permission, and is not
        fundamental to the model, so it is probably better to state it
        separately anyway.

        30.d   Note that implementations (and tools like debuggers) can have
        modes that provide other behaviors in addition.
     NOTES
31   (8) An implementation may provide inter-partition communication
     mechanism(s) via special packages and pragmas.  Standard pragmas for
     distribution and methods for specifying inter-partition communication
     are defined in Annex E, ``Distributed Systems''.  If no such mechanisms
     are provided, then each partition is isolated from all others, and
     behaves as a program in and of itself.

   31.a   Ramification:  Not providing such mechanisms is equivalent to
        disallowing multi-partition programs.

   31.b   An implementation may provide mechanisms to facilitate checking the
        consistency of library units elaborated in different partitions;
        Annex E, ``Distributed Systems'' does so.

32   (9) Partitions are not required to run in separate address spaces.  For
     example, an implementation might support dynamic linking via the
     partition concept.

33   (10) An order of elaboration of library_items that is consistent with
     the partial ordering defined above does not always ensure that each
     library_unit_body is elaborated before any other compilation unit whose
     elaboration necessitates that the library_unit_body be already
     elaborated.  (In particular, there is no requirement that the body of a
     library unit be elaborated as soon as possible after the library_unit_
     declaration is elaborated, unless the pragmas in subclause 10.2.1 are
     used.)

34   (11) A partition (active or otherwise) need not have a main subprogram.
     In such a case, all the work done by the partition would be done by
     elaboration of various library_items, and by tasks created by that
     elaboration.  Passive partitions, which cannot have main subprograms,
     are defined in Annex E, ``Distributed Systems''.

   34.a   Ramification:  The environment task is the outermost semantic level
        defined by the language.

   34.b   Standard has no private part.  This prevents strange
        implementation-dependences involving private children of Standard
        having visibility upon Standard's private part.  It doesn't matter
        where the body of Standard appears in the environment, since it
        doesn't do anything.  See Annex A, ``Predefined Language
        Environment''.

   34.c   Note that elaboration dependence is carefully defined in such a way
        that if (say) the body of something doesn't exist yet, then there is
        no elaboration dependence upon the nonexistent body.  (This follows
        from the fact that ``needed by'' is defined that way, and the
        elaboration dependences caused by a pragma Elaborate or Elaborate_All
        are defined in terms of ``needed by''.)  This property allows us to
        use the environment concept both at compile time and at
        partition-construction time/run time.


                            Extensions to Ada 83

        34.d   {extensions to Ada 83} The concept of partitions is new to Ada
        9X.

        34.e   A main subprogram is now optional.  The language-defined
        restrictions on main subprograms are relaxed.

                         Wording Changes From Ada 83

        34.f   Ada 9X uses the term ``main subprogram'' instead of Ada 83's
        ``main program'' (which was inherited from Pascal).  This is done to
        avoid confusion -- a main subprogram is a subprogram, not a program.
        The program as a whole is an entirely different thing.



10.2.1 Elaboration Control

1   [{elaboration control} This subclause defines pragmas that help control
the elaboration order of library_items.]


                         Language Design Principles

        1.a   The rules governing preelaboration are designed to allow it to
        be done largely by bulk initialization of statically allocated
        storage from information in a ``load module'' created by a linker.
        Some implementations may require run-time code to be executed in some
        cases, but we consider these cases rare enough that we need not
        further complicate the rules.

        1.b   It is important that programs be able to declare data
        structures that are link-time initialized with aggregates, string_
        literals, and concatenations thereof.  It is important to be able to
        write link-time evaluated expressions involving the First, Last, and
        Length attributes of such data structures (including variables),
        because they might be initialized with positional aggregates or
        string_literals, and we don't want the user to have to count the
        elements.  There is no corresponding need for accessing
        discriminants, since they can be initialized with a static constant,
        and then the constant can be referred to elsewhere.  It is important
        to allow link-time initialized data structures involving
        discriminant-dependent components.  It is important to be able to
        write link-time evaluated expressions involving pointers (both access
        values and addresses) to the above-mentioned data structures.

        1.c   The rules also ensure that no Elaboration_Check need be
        performed for calls on library-level subprograms declared within a
        preelaborated package.  This is true also of the Elaboration_Check on
        task activation for library level task types declared in a
        preelaborated package.  However, it is not true of the Elaboration_
        Check on instantiations.

        1.d   A static expression should never prevent a library unit from
        being preelaborable.

                                   Syntax

    2   The form of a pragma Preelaborate is as follows:


3     pragma Preelaborate[(library_unit_name)];

    4   {library unit pragma [Preelaborate]} {pragma, library unit
    [Preelaborate]} A pragma Preelaborate is a library unit pragma.


                               Legality Rules

5   {preelaborable (of an elaborable construct) [distributed]} An elaborable
construct is preelaborable unless its elaboration performs any of the
following actions:

        5.a   Ramification:  A preelaborable construct can be elaborated
        without using any information that is available only at run time.
        Note that we don't try to prevent exceptions in preelaborable
        constructs; if the implementation wishes to generate code to raise an
        exception, that's OK.

        5.b   Because there is no flow of control and there are no calls
        (other than to predefined subprograms), these run-time properties can
        actually be detected at compile time.  This is necessary in order to
        require compile-time enforcement of the rules.

    6  The execution of a statement other than a null_statement.

 6.a    Ramification:  A preelaborable construct can contain labels and
        null_statements.

    7  A call to a subprogram other than a static function.

    8  The evaluation of a primary that is a name of an object, unless
       the name is a static expression, or statically denotes a
       discriminant of an enclosing type.

 8.a    Ramification:  One can evaluate such a name, but not as a
        primary.  For example, one can evaluate an attribute of the
        object.  One can evaluate an attribute_reference, so long as it
        does not denote an object, and its prefix does not disobey any
        of these rules.  For example, Obj'Access, Obj'Unchecked_Access,
        and Obj'Address are generally legal in preelaborated library
        units.

    9  The creation of a default-initialized object [(including a
       component)] of a descendant of a private type, private extension,
       controlled type, task type, or protected type with entry_
       declarations; similarly the evaluation of an extension_aggregate
       with an ancestor subtype_mark denoting a subtype of such a type.

 9.a    Ramification:  One can declare these kinds of types, but one
        cannot create objects of those types.

 9.b    It is also non-preelaborable to create an object if that will
        cause the evaluation of a default expression that will call a
        user-defined function.  This follows from the rule above
        forbidding non-null statements.

 9.c    Reason:  Controlled objects are disallowed because most
        implementations will have to take some run-time action during
        initialization, even if the Initialize procedure is null.

10   A generic body is preelaborable only if elaboration of a corresponding
instance body would not perform any such actions, presuming that the actual
for each formal private type (or extension) is a private type (or extension),
and the actual for each formal subprogram is a user-defined subprogram.
{generic contract issue}

        10.a   Reason:  Without this rule about generics, we would have to
        forbid instantiations in preelaborated library units, which would
        significantly reduce their usefulness.

11   {preelaborated [partial]} If a pragma Preelaborate (or pragma Pure --
see below) applies to a library unit, then it is preelaborated.
[{preelaborated [distributed]} If a library unit is preelaborated, then its
declaration, if any, and body, if any, are elaborated prior to all
non-preelaborated library_items of the partition.]  All compilation units of
a preelaborated library unit shall be preelaborable.  {generic contract issue
[partial]} In addition to the places where Legality Rules normally apply (see
12.3), this rule applies also in the private part of an instance of a generic
unit.  In addition, all compilation units of a preelaborated library unit
shall depend semantically only on compilation units of other preelaborated
library units.

        11.a   Ramification:  In a generic body, we assume the worst about
        formal private types and extensions.
                            Implementation Advice

12   In an implementation, a type declared in a preelaborated package should
have the same representation in every elaboration of a given version of the
package, whether the elaborations occur in distinct executions of the same
program, or in executions of distinct programs or partitions that include the
given version.


                                   Syntax

    13   The form of a pragma Pure is as follows:


14    pragma Pure[(library_unit_name)];

    15   {library unit pragma [Pure]} {pragma, library unit [Pure]} A pragma
    Pure is a library unit pragma.


                               Legality Rules

16   {pure} A pure library_item is a preelaborable library_item that does not
contain the declaration of any variable or named access type, except within a
subprogram, generic subprogram, task unit, or protected unit.

17   {declared pure} A pragma Pure is used to declare that a library unit is
pure.  If a pragma Pure applies to a library unit, then its compilation units
shall be pure, and they shall depend semantically only on compilation units
of other library units that are declared pure.

        17.a   To be honest:  A declared-pure library unit is one to which a
        pragma Pure applies.  Its declaration and body are also said to be
        declared pure.

        17.b   Discussion:  A declared-pure package is useful for defining
        types to be shared between partitions with no common address space.

        17.c   Reason:  Note that generic packages are not mentioned in the
        list of things that can contain variable declarations.  Note that the
        Ada 9X rules for deferred constants make them allowable in library
        units that are declared pure; that isn't true of Ada 83's deferred
        constants.

        17.d   Ramification:  Anonymous access types (that is, access
        discriminants and access parameters) are allowed.

        17.e   Reason:  The primary reason for disallowing named access types
        is that an allocator has a side effect; the pool constitutes variable
        data.  We considered somehow allowing allocator-less access types.
        However, these (including access-to-subprogram types) would cause
        trouble for Annex E, ``Distributed Systems'', because such types
        would allow access values in a shared passive partition to designate
        objects in an active partition, thus allowing inter-address space
        references.  Furthermore, a named access-to-object type without a
        pool would be a new concept, adding complexity from the user's point
        of view.  Finally, the prevention of allocators would have to be a
        run-time check, in order to avoid violations of the generic contract
        model.


                         Implementation Permissions

18   If a library unit is declared pure, then the implementation is permitted
to omit a call on a library-level subprogram of the library unit if the
results are not needed after the call.  Similarly, it may omit such a call
and simply reuse the results produced by an earlier call on the same
subprogram, provided that none of the parameters are of a limited type, and
the addresses and values of all by-reference actual parameters, and the
values of all by-copy-in actual parameters, are the same as they were at the
earlier call.  [This permission applies even if the subprogram produces other
side effects when called.]

        18.a   Discussion:  A declared-pure library_item has no variable
        state.  Hence, a call on one of its (nonnested) subprograms cannot
        ``normally'' have side effects.  The only possible side effects from
        such a call would be through machine code insertions, unchecked
        conversion to an access type declared within the subprogram, and
        similar features.  The compiler may omit a call to such a subprogram
        even if such side effects exist, so the writer of such a subprogram
        has to keep this in mind.


                                   Syntax

    19   The form of a pragma Elaborate, Elaborate_All, or Elaborate_Body is
    as follows:


20    pragma Elaborate(library_unit_name{, library_unit_name});

21    pragma Elaborate_All(library_unit_name{, library_unit_name});

22    pragma Elaborate_Body[(library_unit_name)];

    23   A pragma Elaborate or Elaborate_All is only allowed within a
    context_clause.

        23.a   Ramification:  ``Within a context_clause'' allows it to be the
        last item in the context_clause.  It can't be first, because the name
        has to denote something mentioned earlier.  {94-4910.a}

    24   {library unit pragma [Elaborate_Body]} {pragma, library unit
    [Elaborate_Body]} A pragma Elaborate_Body is a library unit pragma.


        24.a   Discussion:  Hence, a pragma Elaborate or Elaborate_All is not
        elaborated, not that it makes any practical difference.

        24.b   Note that a pragma Elaborate or Elaborate_All is neither a
        program unit pragma, nor a library unit pragma.


                               Legality Rules

25   {requires a completion [declaration to which a pragma Elaborate_Body
applies]} If a pragma Elaborate_Body applies to a declaration, then the
declaration requires a completion [(a body)].


                              Static Semantics

26   [A pragma Elaborate specifies that the body of the named library unit is
elaborated before the current library_item.  A pragma Elaborate_All specifies
that each library_item that is needed by the named library unit declaration
is elaborated before the current library_item.  A pragma Elaborate_Body
specifies that the body of the library unit is elaborated immediately after
its declaration.]

        26.a   Proof:  The official statement of the semantics of these
        pragmas is given in 10.2.

        26.b   Implementation Note:  The presence of a pragma Elaborate_Body
        simplifies the removal of unnecessary Elaboration_Checks.  For a
        subprogram declared immediately within a library unit to which a
        pragma Elaborate_Body applies, the only calls that can fail the
        Elaboration_Check are those that occur in the library unit itself,
        between the declaration and body of the called subprogram; if there
        are no such calls (which can easily be detected at compile time if
        there are no stubs), then no Elaboration_Checks are needed for that
        subprogram.  The same is true for Elaboration_Checks on task
        activations and instantiations, and for library subprograms and
        generic units.

        26.c   Ramification:  The fact that the unit of elaboration is the
        library_item means that if a subprogram_body is not a completion, it
        is impossible for any library_item to be elaborated between the
        declaration and the body of such a subprogram.  Therefore, it is
        impossible for a call to such a subprogram to fail its Elaboration_
        Check.

        26.d   Discussion:  The visibility rules imply that each library_
        unit_name of a pragma Elaborate or Elaborate_All has to denote a
        library unit mentioned by a previous with_clause of the same context_
        clause.


     NOTES
27   (12) A preelaborated library unit is allowed to have non-preelaborable
     children.

   27.a   Ramification:  But not non-preelaborated subunits.

28   (13) A library unit that is declared pure is allowed to have impure
     children.

   28.a   Ramification:  But not impure subunits.

   28.b   Ramification:  Pragma Elaborate is mainly for closely related
        library units, such as when two package bodies 'with' each other's
        declarations.  In such cases, Elaborate_All sometimes won't work.


                            Extensions to Ada 83

        28.c   {extensions to Ada 83} The concepts of preelaborability and
        purity are new to Ada 9X.  The Elaborate_All, Elaborate_Body,
        Preelaborate, and Pure pragmas are new to Ada 9X.

        28.d   Pragmas Elaborate are allowed to be mixed in with the other
        things in the context_clause -- in Ada 83, they were required to
        appear last.



                           Section 11: Exceptions


1   [This section defines the facilities for dealing with errors or other
exceptional situations that arise during program execution.] {exception
occurrence} {condition: see also exception} {signal (an exception): see
raise} {throw (an exception): see raise} {catch (an exception): see handle}
{Exception} [glossary entry]An exception represents a kind of exceptional
situation; an occurrence of such a situation (at run time) is called an
exception occurrence.[ {raise [an exception]} To raise an exception is to
abandon normal program execution so as to draw attention to the fact that the
corresponding situation has arisen.  {handle [an exception]} Performing some
actions in response to the arising of an exception is called handling the
exception.]
        1.a   To be honest:  {handle [an exception occurrence]} ...or
        handling the exception occurrence.

        1.b   Ramification:  For example, an exception End_Error might
        represent error situations in which an attempt is made to read beyond
        end-of-file.  During the execution of a partition, there might be
        numerous occurrences of this exception.

        1.c   To be honest:  {occurrence (of an exception)} When the meaning
        is clear from the context, we sometimes use ``occurrence'' as a
        short-hand for ``exception occurrence.''

2   [An exception_declaration declares a name for an exception.  An exception
is raised initially either by a raise_statement or by the failure of a
language-defined check.  When an exception arises, control can be transferred
to a user-provided exception_handler at the end of a handled_sequence_of_
statements, or it can be propagated to a dynamically enclosing execution.]


                         Wording Changes From Ada 83

        2.a   We are more explicit about the difference between an exception
        and an occurrence of an exception.  This is necessary because we now
        have a type (Exception_Occurrence) that represents exception
        occurrences, so the program can manipulate them.  Furthermore, we say
        that when an exception is propagated, it is the same occurrence that
        is being propagated (as opposed to a new occurrence of the same
        exception).  The same issue applies to a re-raise statement.  In
        order to understand these semantics, we have to make this
        distinction.



11.1 Exception Declarations

1   {exception} An exception_declaration declares a name for an exception.


                                   Syntax

2   exception_declaration ::= defining_identifier_list : exception;


                              Static Semantics

3   Each single exception_declaration declares a name for a different
exception.  If a generic unit includes an exception_declaration, the
exception_declarations implicitly generated by different instantiations of
the generic unit refer to distinct exceptions (but all have the same
defining_identifier).

        3.a   Reason:  We considered removing this requirement inside generic
        bodies, because it is an implementation burden for implementations
        that wish to share code among several instances.  In the end, it was
        decided that it would introduce too much implementation dependence.

The particular exception denoted by an exception name is determined at
compilation time and is the same regardless of how many times the exception_
declaration is elaborated.

        3.b   Ramification:  Hence, if an exception_declaration occurs in a
        recursive subprogram, the exception name denotes the same exception
        for all invocations of the recursive subprogram.  The reason for this
        rule is that we allow an exception occurrence to propagate out of its
        declaration's innermost containing master; if exceptions were created
        by their declarations like other entities, they would presumably be
        destroyed upon leaving the master; we would have to do something
        special to prevent them from propagating to places where they no
        longer exist.

        3.c   Ramification:  Exception identities are unique across all
        partitions of a program.

4   {predefined exception} {Constraint_Error (raised by failure of run-time
check)} {Program_Error (raised by failure of run-time check)} {Storage_Error
(raised by failure of run-time check)} {Tasking_Error (raised by failure of
run-time check)} The predefined exceptions are the ones declared in the
declaration of package Standard:  Constraint_Error, Program_Error, Storage_
Error, and Tasking_Error[; one of them is raised when a language-defined
check fails.]

        4.a   Ramification:  The exceptions declared in the language-defined
        package IO_Exceptions, for example, are not predefined.


                              Dynamic Semantics

5   {elaboration [exception_declaration]} The elaboration of an exception_
declaration has no effect.

6   {Storage_Check [partial]} {check, language-defined (Storage_Check)}
{Storage_Error (raised by failure of run-time check)} The execution of any
construct raises Storage_Error if there is insufficient storage for that
execution.  {unspecified [partial]} The amount of storage needed for the
execution of constructs is unspecified.

        6.a   Ramification:  Note that any execution whatsoever can raise
        Storage_Error.  This allows much implementation freedom in storage
        management.


                                  Examples

7   Examples of user-defined exception declarations:

8   Singular : exception;
    Error    : exception;
    Overflow, Underflow : exception;


                         Inconsistencies With Ada 83

        8.a   {inconsistencies with Ada 83} The exception Numeric_Error is
        now defined in the Obsolescent features Annex, as a rename of
        Constraint_Error.  All checks that raise Numeric_Error in Ada 83
        instead raise Constraint_Error in Ada 9X.  To increase upward
        compatibility, we also changed the rules to allow the same exception
        to be named more than once by a given handler.  Thus, ``when
        Constraint_Error | Numeric_Error =>'' will remain legal in Ada 9X,
        even though Constraint_Error and Numeric_Error now denote the same
        exception.  However, it will not be legal to have separate handlers
        for Constraint_Error and Numeric_Error.  This change is inconsistent
        in the rare case that an existing program explicitly raises Numeric_
        Error at a point where there is a handler for Constraint_Error; the
        exception will now be caught by that handler.

                         Wording Changes From Ada 83

        8.b   We explicitly define elaboration for exception_declarations.



11.2 Exception Handlers

1   [The response to one or more exceptions is specified by an exception_
handler.]


                                   Syntax

2   handled_sequence_of_statements ::=
         sequence_of_statements
      [exception
         exception_handler
        {exception_handler}]

3   exception_handler ::=
      when [choice_parameter_specification:] exception_choice {| exception_choi\
ce} =>
         sequence_of_statements

4   choice_parameter_specification ::= defining_identifier

5   exception_choice ::= exception_name | others

        5.a   To be honest:  {handler} ``Handler'' is an abbreviation for
        ``exception_handler.''

        5.b   {choice (of an exception_handler)} Within this section, we
        sometimes abbreviate ``exception_choice'' to ``choice.''


                               Legality Rules

6   {cover (of a choice and an exception)} A choice with an exception_name
covers the named exception.  A choice with others covers all exceptions not
named by previous choices of the same handled_sequence_of_statements.  Two
choices in different exception_handlers of the same handled_sequence_of_
statements shall not cover the same exception.

        6.a   Ramification:  Two choices of the same exception_handler may
        cover the same exception.  For example, given two renaming
        declarations in separate packages for the same exception, one may
        nevertheless write, for example, ``when Ada.Text_IO.Data_Error | My_
        Seq_IO.Data_Error =>''.

        6.b   An others choice even covers exceptions that are not visible at
        the place of the handler.  Since exception raising is a dynamic
        activity, it is entirely possible for an others handler to handle an
        exception that it could not have named.

7   A choice with others is allowed only for the last handler of a handled_
sequence_of_statements and as the only choice of that handler.

8   An exception_name of a choice shall not denote an exception declared in a
generic formal package.

        8.a   Reason:  This is because the compiler doesn't know the identity
        of such an exception, and thus can't enforce the coverage rules.


                              Static Semantics

9   {choice parameter} A choice_parameter_specification declares a choice
parameter, which is a constant object of type Exception_Occurrence (see
11.4.1).  During the handling of an exception occurrence, the choice
parameter, if any, of the handler represents the exception occurrence that is
being handled.
                              Dynamic Semantics

10   {execution [handled_sequence_of_statements]} The execution of a handled_
sequence_of_statements consists of the execution of the sequence_of_
statements.  [The optional handlers are used to handle any exceptions that
are propagated by the sequence_of_statements.]


                                  Examples

11   Example of an exception handler:  {94-4771.a}

12  begin
       Open(File, In_File, "input.txt");   -- see A.8.2
    exception
       when E : Name_Error =>
          Put("Cannot open input file : ");
          Put_Line(Exception_Message(E));  -- see 11.4.1
          raise;
    end;


                            Extensions to Ada 83

        12.a   {extensions to Ada 83} The syntax rule for exception_handler
        is modified to allow a choice_parameter_specification.

        12.b   Different choices of the same exception_handler may cover the
        same exception.  This allows for ``when Numeric_Error | Constraint_
        Error =>'' even though Numeric_Error is a rename of Constraint_Error.
        This also allows one to ``with'' two different I/O packages, and then
        write, for example, ``when Ada.Text_IO.Data_Error | My_Seq_IO.Data_
        Error =>'' even though these might both be renames of the same
        exception.

                         Wording Changes From Ada 83

        12.c   The syntax rule for handled_sequence_of_statements is new.
        These are now used in all the places where handlers are allowed.
        This obviates the need to explain (in Sections 5, 6, 7, and 9) what
        portions of the program are handled by the handlers.  Note that there
        are more such cases in Ada 9X.

        12.d   The syntax rule for choice_parameter_specification is new.



11.3 Raise Statements

1   [A raise_statement raises an exception.]


                                   Syntax

2   raise_statement ::= raise [exception_name];


                               Legality Rules

3   The name, if any, in a raise_statement shall denote an exception.
{re-raise statement} A raise_statement with no exception_name (that is, a
re-raise statement) shall be within a handler, but not within a body enclosed
by that handler.


                              Dynamic Semantics

4   {raise (an exception)} To raise an exception is to raise a new occurrence
of that exception[, as explained in 11.4].  {execution [raise_statement with
an exception_name]} For the execution of a raise_statement with an
exception_name, the named exception is raised.  {execution [re-raise
statement]} For the execution of a re-raise statement, the exception
occurrence that caused transfer of control to the innermost enclosing handler
is raised [again].

        4.a   Implementation Note:  For a re-raise statement, the
        implementation does not create a new Exception_Occurrence, but
        instead propagates the same Exception_Occurrence value.  This allows
        the original cause of the exception to be determined.


                                  Examples

5   Examples of raise statements:

6   raise Ada.IO_Exceptions.Name_Error;   -- see A.13

7   raise;                                -- re-raise the current exception


                         Wording Changes From Ada 83

        7.a   The fact that the name in a raise_statement has to denote an
        exception is not clear from RM83.  Clearly that was the intent, since
        the italicized part of the syntax rules so indicate, but there was no
        explicit rule.  RM83-1.5(11) doesn't seem to give the italicized
        parts of the syntax any force.



11.4 Exception Handling

1   [When an exception occurrence is raised, normal program execution is
abandoned and control is transferred to an applicable exception_handler, if
any.  {handle (an exception occurrence)} To handle an exception occurrence is
to respond to the exceptional event.  {propagate} To propagate an exception
occurrence is to raise it again in another context; that is, to fail to
respond to the exceptional event in the present context.]

        1.a   Ramification:  In other words, if the execution of a given
        construct raises an exception, but does not handle it, the exception
        is propagated to an enclosing execution (except in the case of a
        task_body).

        1.b   Propagation involves re-raising the same exception occurrence
        (assuming the implementation has not taken advantage of the
        Implementation Permission of 11.3).  For example, calling an entry of
        an uncallable task raises Tasking_Error; this is not propagation.


                              Dynamic Semantics

2   {dynamically enclosing (of one execution by another)} {execution
(dynamically enclosing)} Within a given task, if the execution of construct a
is defined by this International Standard to consist (in part) of the
execution of construct b, then while b is executing, the execution of a is
said to dynamically enclose the execution of b.  {innermost dynamically
enclosing} The innermost dynamically enclosing execution of a given execution
is the dynamically enclosing execution that started most recently.

        2.a   To be honest:  {included (one execution by another)} {execution
        (included by another execution)} If the execution of a dynamically
        encloses that of b, then we also say that the execution of b is
        included in the execution of a.

        2.b   Ramification:  Examples: The execution of an if_statement
        dynamically encloses the evaluation of the condition after the if
        (during that evaluation).  (Recall that ``execution'' includes both
        ``elaboration'' and ``evaluation'', as well as other executions.)
        The evaluation of a function call dynamically encloses the execution
        of the sequence_of_statements of the function_body (during that
        execution).  Note that, due to recursion, several simultaneous
        executions of the same construct can be occurring at once during the
        execution of a particular task.

        2.c   Dynamically enclosing is not defined across task boundaries; a
        task's execution does not include the execution of any other tasks.

        2.d   Dynamically enclosing is only defined for executions that are
        occurring at a given moment in time; if an if_statement is currently
        executing the sequence_of_statements after then, then the evaluation
        of the condition is no longer dynamically enclosed by the execution
        of the if_statement (or anything else).

3   {raise (an exception occurrence)} When an exception occurrence is raised
by the execution of a given construct, the rest of the execution of that
construct is abandoned; that is, any portions of the execution that have not
yet taken place are not performed.  The construct is first completed, and
then left, as explained in 7.6.1.  Then:

    4  If the construct is a task_body, the exception does not propagate
       further;

 4.a    Ramification:  When an exception is raised by the execution of a
        task_body, there is no dynamically enclosing execution, so the
        exception does not propagate any further.  If the exception
        occurred during the activation of the task, then the activator
        raises Tasking_Error, as explained in 9.2, ``Task Execution -
        Task Activation'', but we don't define that as propagation; it's
        a special rule.  Otherwise (the exception occurred during the
        execution of the handled_sequence_of_statements of the task),
        the task silently disappears.  Thus, abnormal termination of
        tasks is not always considered to be an error.

    5  If the construct is the sequence_of_statements of a handled_
       sequence_of_statements that has a handler with a choice covering
       the exception, the occurrence is handled by that handler;

    6  {propagate (an exception occurrence by an execution, to a
       dynamically enclosing execution)} Otherwise, the occurrence is
       propagated to the innermost dynamically enclosing execution,
       which means that the occurrence is raised again in that context.

 6.a    To be honest:  {propagate (an exception by an execution)}
        {propagate (an exception by a construct)} As shorthands, we
        refer to the propagation of an exception, and the propagation by
        a construct, if the execution of the construct propagates an
        exception occurrence.

7   {handle (an exception occurrence)} {execution [handler]} {elaboration
[choice_parameter_specification]} When an occurrence is handled by a given
handler, the choice_parameter_specification, if any, is first elaborated,
which creates the choice parameter and initializes it to the occurrence.
Then, the sequence_of_statements of the handler is executed; this execution
replaces the abandoned portion of the execution of the sequence_of_
statements.

        7.a   Ramification:  This ``replacement'' semantics implies that the
        handler can do pretty much anything the abandoned sequence could do;
        for example, in a function, the handler can execute a return_
        statement that applies to the function.

        7.b   Ramification:  The rules for exceptions raised in library
        units, main subprograms and partitions follow from the normal rules,
        plus the semantics of the environment task described in Section 10
        (for example, the environment task of a partition elaborates library
        units and calls the main subprogram).  If an exception is propagated
        by the main subprogram, it is propagated to the environment task,
        which then terminates abnormally, causing the partition to terminate
        abnormally.  Although abnormal termination of tasks is not
        necessarily an error, abnormal termination of a partition due to an
        exception is an error.


     NOTES
8    (1) Note that exceptions raised in a declarative_part of a body are not
     handled by the handlers of the handled_sequence_of_statements of that
     body.



11.4.1 The Package Exceptions

                              Static Semantics

1   The following language-defined library package exists:

2   package Ada.Exceptions is
        type Exception_Id is private;
        Null_Id : constant Exception_Id;
        function Exception_Name(Id : Exception_Id) return String;

3       type Exception_Occurrence is limited private;
        type Exception_Occurrence_Access is access all Exception_Occurrence;
        Null_Occurrence : constant Exception_Occurrence;

4       procedure Raise_Exception(E : in Exception_Id; Message : in String := "\
");
        function Exception_Message(X : Exception_Occurrence) return String;
        procedure Reraise_Occurrence(X : in Exception_Occurrence);

5       function Exception_Identity(X : Exception_Occurrence) return Exception_\
Id;
        function Exception_Name(X : Exception_Occurrence) return String;
            -- Same as Exception_Name(Exception_Identity(X)).
        function Exception_Information(X : Exception_Occurrence) return String;

6       procedure Save_Occurrence(Target : out Exception_Occurrence;
                                  Source : in Exception_Occurrence);
        function Save_Occurrence(Source : Exception_Occurrence)
                                 return Exception_Occurrence_Access;
    private
       ... -- not specified by the language
    end Ada.Exceptions;

7   Each distinct exception is represented by a distinct value of type
Exception_Id.  Null_Id does not represent any exception, and is the default
initial value of type Exception_Id.  Each occurrence of an exception is
represented by a value of type Exception_Occurrence.  Null_Occurrence does
not represent any exception occurrence, and is the default initial value of
type Exception_Occurrence.

8   For a prefix E that denotes an exception, the following attribute is
defined:

9   E'Identity
                E'Identity returns the unique identity of the exception.  The
                type of this attribute is Exception_Id.

9.a     Ramification:  In a distributed program, the identity is unique
        across an entire program, not just across a single partition.
        Exception propagation works properly across RPC's.  An exception can
        be propagated from one partition to another, and then back to the
        first, where its identity is known.

10   Raise_Exception raises a new occurrence of the identified exception.  In
this case, Exception_Message returns the Message parameter of Raise_
Exception.  For a raise_statement with an exception_name, Exception_Message
returns implementation-defined information about the exception occurrence.
Reraise_Occurrence reraises the specified exception occurrence.

        10.a   Implementation defined:  The information returned by
        Exception_Message.

        10.b   Ramification:  Given an exception E, the raise_statement:

10.c        raise E;

        10.d   is equivalent to this call to Raise_Exception:

10.e        Raise_Exception(E'Identity, Message => implementation-defined-strin\
g);

        10.f   The following handler:

10.g        when others =>
                Cleanup;
                raise;

        10.h   is equivalent to this one:

10.i        when X : others =>
                Cleanup;
                Reraise_Occurrence(X);

11   Exception_Identity returns the identity of the exception of the
occurrence.

12   The Exception_Name functions return the full expanded name of the
exception, in upper case, starting with a root library unit.  For an
exception declared immediately within package Standard, the defining_
identifier is returned.  {94-4774.d} {94-4828.d} The result is implementation
defined if the exception is declared within an unnamed block_statement.

        12.a   Ramification:  See the Implementation Permission below.

        12.b   To be honest:  This name, as well as each prefix of it, does
        not denote a renaming_declaration.

        12.c   Implementation defined:  The result of Exceptions.Exception_
        Name for types declared within an unnamed block_statement.

        12.d   Ramification:  Note that we're talking about the name of the
        exception, not the name of the occurrence.

13   Exception_Information returns implementation-defined information about
the exception occurrence.

        13.a   Implementation defined:  The information returned by
        Exception_Information.

14   Raise_Exception and Reraise_Occurrence have no effect in the case of
Null_Id or Null_Occurrence.  {Constraint_Error (raised by failure of run-time
check)} Exception_Message, Exception_Identity, Exception_Name, and Exception_
Information raise Constraint_Error for a Null_Id or Null_Occurrence.

15   The Save_Occurrence procedure copies the Source to the Target.  The
Save_Occurrence function uses an allocator of type Exception_Occurrence_
Access to create a new object, copies the Source to this new object, and
returns an access value designating this new object; [the result may be
deallocated using an instance of Unchecked_Deallocation.]

        15.a   Ramification:  It's OK to pass Null_Occurrence to the Save_
        Occurrence subprograms; they don't raise an exception, but simply
        save the Null_Occurrence.


                         Implementation Requirements

16   The implementation of the Write attribute (see 13.13.2) of Exception_
Occurrence shall support writing a representation of an exception occurrence
to a stream; the implementation of the Read attribute of Exception_Occurrence
shall support reconstructing an exception occurrence from a stream (including
one written in a different partition).

        16.a   Ramification:  The identity of the exception, as well as the
        Exception_Name and Exception_Message, have to be preserved across
        partitions.

        16.b   The string returned by Exception_Name or Exception_Message on
        the result of calling the Read attribute on a given stream has to be
        the same as the value returned by calling the corresponding function
        on the exception occurrence that was written into the stream with the
        Write attribute.  The string returned by Exception_Information need
        not be the same, since it is implementation defined anyway.

        16.c   Reason:  This is important for supporting writing exception
        occurrences to external files for post-mortem analysis, as well as
        propagating exceptions across remote subprogram calls in a
        distributed system (see E.4).


                         Implementation Permissions

17   An implementation of Exception_Name in a space-constrained environment
may return the defining_identifier instead of the full expanded name.

18   The string returned by Exception_Message may be truncated (to no less
than 200 characters) by the Save_Occurrence procedure [(not the function)],
the Reraise_Occurrence procedure, and the re-raise statement.

        18.a   Reason:  The reason for allowing truncation is to ease
        implementations.  The reason for choosing the number 200 is that this
        is the minimum source line length that implementations have to
        support, and this feature seems vaguely related since it's usually a
        ``one-liner''.  Note that an implementation is allowed to do this
        truncation even if it supports arbitrarily long lines.


                            Implementation Advice

19   Exception_Message (by default) and Exception_Information should produce
information useful for debugging.  Exception_Message should be short (about
one line), whereas Exception_Information can be long.  Exception_Message
should not include the Exception_Name.  Exception_Information should include
both the Exception_Name and the Exception_Message.  {94-4912.a}

        19.a   Reason:  It may seem strange to define two subprograms whose
        semantics is implementation defined.  The idea is that a program can
        print out debugging/error-logging information in a portable way.  The
        program is portable in the sense that it will work in any
        implementation; it might print out different information, but the
        presumption is that the information printed out is appropriate for
        debugging/error analysis on that system.

        19.b   Implementation Note:  As an example, Exception_Information
        might include information identifying the location where the
        exception occurred, and, for predefined exceptions, the specific kind
        of language-defined check that failed.  There is an implementation
        trade-off here, between how much information is represented in an
        Exception_Occurrence, and how much can be passed through a re-raise.

        19.c   The string returned should be in a form suitable for printing
        to an error log file.  This means that it might need to contain
        line-termination control characters with implementation-defined I/O
        semantics.  The string should neither start nor end with a newline.
        {94-4912.a}

        19.d   If an implementation chooses to provide additional
        functionality related to exceptions and their occurrences, it should
        do so by providing one or more children of Ada.Exceptions.

        19.e   Note that exceptions behave as if declared at library level;
        there is no ``natural scope'' for an exception; an exception always
        exists.  Hence, there is no harm in saving an exception occurrence in
        a data structure, and reraising it later.  The reraise has to occur
        as part of the same program execution, so saving an exception
        occurrence in a file, reading it back in from a different program
        execution, and then reraising it is not required to work.  This is
        similar to I/O of access types.  Note that it is possible to use RPC
        to propagate exceptions across partitions.

        19.f   Here's one way to implement Exception_Occurrence in the
        private part of the package.  Using this method, an implementation
        need store only the actual number of characters in exception
        messages.  If the user always uses small messages, then exception
        occurrences can be small.  If the user never uses messages, then
        exception occurrences can be smaller still:

19.g        type Exception_Occurrence(Message_Length : Natural := 200) is
                limited record
                    Id : Exception_Id;
                    Message : String(1..Message_Length);
                end record;

        19.h   At the point where an exception is raised, an Exception_
        Occurrence can be allocated on the stack with exactly the right
        amount of space for the message -- none for an empty message.  This
        is just like declaring a constrained object of the type:

19.i        Temp : Exception_Occurrence(10); -- for a 10-character message

        19.j   After finding the appropriate handler, the stack can be cut
        back, and the Temp copied to the right place.  This is similar to
        returning an unknown-sized object from a function.  It is not
        necessary to allocate the maximum possible size for every Exception_
        Occurrence.  If, however, the user declares an Exception_Occurrence
        object, the discriminant will be permanently set to 200.  The Save_
        Occurrence procedure would then truncate the Exception_Message.
        Thus, nothing is lost until the user tries to save the occurrence.
        If the user is willing to pay the cost of heap allocation, the Save_
        Occurrence function can be used instead.

        19.k   Note that any arbitrary-sized implementation-defined
        Exception_Information can be handled in a similar way.  For example,
        if the Exception_Occurrence includes a stack traceback, a
        discriminant can control the number of stack frames stored.  The
        traceback would be truncated or entirely deleted by the Save_
        Occurrence procedure -- as the implementation sees fit.

        19.l   If the internal representation involves pointers to data
        structures that might disappear, it would behoove the implementation
        to implement it as a controlled type, so that assignment can either
        copy the data structures or else null out the pointers.
        Alternatively, if the data structures being pointed at are in a task
        control block, the implementation could keep a unique sequence number
        for each task, so it could tell when a task's data structures no
        longer exist.

        19.m   Using the above method, heap space is never allocated unless
        the user calls the Save_Occurrence function.

        19.n   An alternative implementation would be to store the message
        strings on the heap when the exception is raised.  (It could be the
        global heap, or it could be a special heap just for this purpose --
        it doesn't matter.)  This representation would be used only for
        choice parameters.  For normal user-defined exception occurrences,
        the Save_Occurrence procedure would copy the message string into the
        occurrence itself, truncating as necessary.  Thus, in this
        implementation, Exception_Occurrence would be implemented as a
        variant record:

19.o        type Exception_Occurrence_Kind is (Normal, As_Choice_Param);

19.p        type Exception_Occurrence(Kind : Exception_Occurrence_Kind := Norma\
l) is
                limited record
                    case Kind is
                        when Normal =>
                            ... -- space for 200 characters
                        when As_Choice_Param =>
                            ... -- pointer to heap string
                    end case;
                end record;

        19.q   Exception_Occurrences created by the run-time system during
        exception raising would be As_Choice_Param.  User-declared ones would
        be Normal -- the user cannot see the discriminant, and so cannot set
        it to As_Choice_Param.  The strings in the heap would be freed upon
        completion of the handler.

        19.r   This alternative implementation corresponds to a heap-based
        implementation of functions returning unknown-sized results.

        19.s   One possible implementation of Reraise_Occurrence is as
        follows:

19.t        procedure Reraise_Occurrence(X : in Exception_Occurrence) is
            begin
                Raise_Exception(Identity(X), Exception_Message(X));
            end Reraise_Occurrence;

        19.u   However, some implementations may wish to retain more
        information across a re-raise -- a stack traceback, for example.

        19.v   Ramification:  Note that Exception_Occurrence is a definite
        subtype.  Hence, values of type Exception_Occurrence may be written
        to an error log for later analysis, or may be passed to subprograms
        for immediate error analysis.

        19.w   Implementation Note:  If an implementation chooses to have a
        mode in which it supports non-Latin-1 characters in identifiers, then
        it needs to define what the above functions return in the case where
        the name of an exception contains such a character.


                            Extensions to Ada 83

        19.x   {extensions to Ada 83} The Identity attribute of exceptions is
        new, as is the package Exceptions.



11.4.2 Example of Exception Handling

                                  Examples

1   Exception handling may be used to separate the detection of an error from
the response to that error:

2   with Ada.Exceptions;
    use Ada;
    package File_System is
        type File_Handle is limited private;

3       File_Not_Found : exception;
        procedure Open(F : in out File_Handle; Name : String);
            -- raises File_Not_Found if named file does not exist

4       End_Of_File : exception;
        procedure Read(F : in out File_Handle; Data : out Data_Type);
            -- raises End_Of_File if the file is not open

5       ...
    end File_System;

6   package body File_System is
        procedure Open(F : in out File_Handle; Name : String) is
        begin
            if File_Exists(Name) then
                ...
            else
                Exceptions.Raise_Exception(File_Not_Found'Identity,
                                          "File not found: " & Name & ".");
            end if;
        end Open;

7       procedure Read(F : in out File_Handle; Data : out Data_Type) is
        begin
            if F.Current_Position <= F.Last_Position then
                ...
            else
                raise End_Of_File;
            end if;
        end Read;

8       ...

9   end File_System;

10  with Ada.Text_IO;
    with Ada.Exceptions;
    with File_System; use File_System;
    use Ada;
    procedure Main is
    begin
        ... -- call operations in File_System
    exception
        when End_Of_File =>
            Close(Some_File);
        when Not_Found_Error : File_Not_Found =>
            Text_IO.Put_Line(Exceptions.Exception_Message(Not_Found_Error));
        when The_Error : others =>
            Text_IO.Put_Line("Unknown error:");
            if Verbosity_Desired then
                Text_IO.Put_Line(Exceptions.Exception_Information(The_Error));
            else
                Text_IO.Put_Line(Exceptions.Exception_Name(The_Error));
                Text_IO.Put_Line(Exceptions.Exception_Message(The_Error));
            end if;
            raise;
    end Main;

{94-4556.a} {94-4561.a} {94-5000.g} {94-5001.i}

11   In the above example, the File_System package contains information about
detecting certain exceptional situations, but it does not specify how to
handle those situations.  Procedure Main specifies how to handle them; other
clients of File_System might have different handlers, even though the
exceptional situations arise from the same basic causes.


                         Wording Changes From Ada 83

        11.a   The sections labeled ``Exceptions Raised During ...''  are
        subsumed by this clause, and by parts of Section 9.



11.5 Suppressing Checks

1   A pragma Suppress gives permission to an implementation to omit certain
language-defined checks.

2   {language-defined check} {check (language-defined)} {run-time check: see
language-defined check} {run-time error} {error (run-time)} A
language-defined check (or simply, a ``check'') is one of the situations
defined by this International Standard that requires a check to be made at
run time to determine whether some condition is true.  {failure (of a
language-defined check)} A check fails when the condition being checked is
false, causing an exception to be raised.

        2.a   Discussion:  All such checks are defined under ``Dynamic
        Semantics'' in clauses and subclauses throughout the standard.


                                   Syntax

    3   The form of a pragma Suppress is as follows:


4     pragma Suppress(identifier [, [On =>] name]);

    5   {configuration pragma [Suppress]} {pragma, configuration [Suppress]}
    A pragma Suppress is allowed only immediately within a declarative_part,
    immediately within a package_specification, or as a configuration pragma.


                               Legality Rules

6   The identifier shall be the name of a check.  The name (if present) shall
statically denote some entity.

7   For a pragma Suppress that is immediately within a package_specification
and includes a name, the name shall denote an entity (or several overloaded
subprograms) declared immediately within the package_specification.


                              Static Semantics

8   A pragma Suppress gives permission to an implementation to omit the named
check from the place of the pragma to the end of the innermost enclosing
declarative region, or, if the pragma is given in a package_specification and
includes a name, to the end of the scope of the named entity.  If the pragma
includes a name, the permission applies only to checks performed on the named
entity, or, for a subtype, on objects and values of its type.  Otherwise, the
permission applies to all entities.  {suppressed check} If permission has
been given to suppress a given check, the check is said to be suppressed.

        8.a   Ramification:  A check is suppressed even if the implementation
        chooses not to actually generate better code.  {Program_Error (raised
        by failure of run-time check)} This allows the implementation to
        raise Program_Error, for example, if the erroneousness is detected.

9   The following are the language-defined checks:

   10  {Constraint_Error (raised by failure of run-time check)} [The
       following checks correspond to situations in which the exception
       Constraint_Error is raised upon failure.]

11       {Access_Check [distributed]} Access_Check
                       [When evaluating a dereference (explicit or
                       implicit), check that the value of the name is
                       not null.  When passing an actual parameter to a
                       formal access parameter, check that the value of
                       the actual parameter is not null.]

12       {Discriminant_Check [distributed]} Discriminant_
                       Check
                       [Check that the discriminants of a composite
                       value have the values imposed by a discriminant
                       constraint.  Also, when accessing a record
                       component, check that it exists for the current
                       discriminant values.]

13       {Division_Check [distributed]} Division_Check
                       [Check that the second operand is not zero for
                       the operations /, rem and mod.]

14       {Index_Check [distributed]} Index_Check
                       [Check that the bounds of an array value are
                       equal to the corresponding bounds of an index
                       constraint.  Also, when accessing a component of
                       an array object, check for each dimension that
                       the given index value belongs to the range
                       defined by the bounds of the array object.  Also,
                       when accessing a slice of an array object, check
                       that the given discrete range is compatible with
                       the range defined by the bounds of the array
                       object.]

15       {Length_Check [distributed]} Length_Check
                       [Check that two arrays have matching components,
                       in the case of array subtype conversions, and
                       logical operators for arrays of boolean
                       components.]

16       {Overflow_Check [distributed]} Overflow_Check
                       [Check that a scalar value is within the base
                       range of its type, in cases where the
                       implementation chooses to raise an exception
                       instead of returning the correct mathematical
                       result.]

17       {Range_Check [distributed]} Range_Check
                       [Check that a scalar value satisfies a range
                       constraint.  Also, for the elaboration of a
                       subtype_indication, check that the constraint (if
                       present) is compatible with the subtype denoted
                       by the subtype_mark.  Also, for an aggregate,
                       check that an index or discriminant value belongs
                       to the corresponding subtype.  Also, check that
                       when the result of an operation yields an array,
                       the value of each component belongs to the
                       component subtype.]

18       {Tag_Check [distributed]} Tag_Check
                       [Check that operand tags in a dispatching call
                       are all equal.  Check for the correct tag on
                       tagged type conversions, for an assignment_
                       statement, and when returning a tagged limited
                       object from a function.]

   19  {Program_Error (raised by failure of run-time check)} [The
       following checks correspond to situations in which the exception
       Program_Error is raised upon failure.]

20       {Elaboration_Check [distributed]} Elaboration_
                       Check
                       [When a subprogram or protected entry is called,
                       a task activation is accomplished, or a generic
                       instantiation is elaborated, check that the body
                       of the corresponding unit has already been
                       elaborated.]

21       {Accessibility_Check [distributed]}
                       Accessibility_Check
                       [Check the accessibility level of an entity or
                       view.]  {94-4715.a}

   22  [The following check corresponds to situations in which the
       exception Storage_Error is raised upon failure.]

23       {Storage_Check [distributed]} {Storage_Error
                       (raised by failure of run-time check)} Storage_
                       Check
                       [Check that evaluation of an allocator does not
                       require more space than is available for a
                       storage pool.  Check that the space available for
                       a task or subprogram has not been exceeded.]

23.a    Reason:  We considered splitting this out into three categories:
        Pool_Check (for allocators), Stack_Check (for stack usage), and
        Heap_Check (for implicit use of the heap -- use of the heap
        other than through an allocator).  Storage_Check would then
        represent the union of these three.  However, there seems to be
        no compelling reason to do this, given that it is not feasible
        to split Storage_Error.

   24  [The following check corresponds to all situations in which any
       predefined exception is raised.]

25       {All_Checks [distributed]} All_Checks
                       Represents the union of all checks; [suppressing
                       All_Checks suppresses all checks.]

25.a    Ramification:  All_Checks includes both language-defined and
        implementation-defined checks.


                             Erroneous Execution

26   {erroneous execution} If a given check has been suppressed, and the
corresponding error situation occurs, the execution of the program is
erroneous.


                         Implementation Permissions

27   An implementation is allowed to place restrictions on Suppress pragmas.
An implementation is allowed to add additional check names, with
implementation-defined semantics.  {unspecified [partial]} When Overflow_
Check has been suppressed, an implementation may also suppress an unspecified
subset of the Range_Checks.

        27.a   Reason:  The permission to restrict is given so the
        implementation can give an error message when the requested
        suppression is nonsense, such as suppressing a Range_Check on a task
        type.  It would be verbose and pointless to list all the cases of
        nonsensical language-defined checks in the standard, and since the
        list of checks is open-ended, we can't list the restrictions for
        implementation-defined checks anyway.

        27.b   Implementation defined:  Implementation-defined check names.

        27.c   Discussion:  For Overflow_Check, the intention is that the
        implementation will suppress any Range_Checks that are implemented in
        the same manner as Overflow_Checks (unless they are free).


                            Implementation Advice

28   The implementation should minimize the code executed for checks that
have been suppressed.

        28.a   Implementation Note:  However, if a given check comes for free
        (for example, the hardware automatically performs the check in
        parallel with doing useful work) or nearly free (for example, the
        check is a tiny portion of an expensive run-time system call), the
        implementation should not bother to suppress the check.  Similarly,
        if the implementation detects the failure at compile time and
        provides a warning message, there is no need to actually suppress the
        check.  {94-4501.a}


     NOTES
29   (2) {optimization} {efficiency} There is no guarantee that a suppressed
     check is actually removed; hence a pragma Suppress should be used only
     for efficiency reasons.


                                  Examples

30   Examples of suppressing checks:

31  pragma Suppress(Range_Check);
    pragma Suppress(Index_Check, On => Table);


                            Extensions to Ada 83

        31.a   {extensions to Ada 83} A pragma Suppress is allowed as a
        configuration pragma.  A pragma Suppress without a name is allowed in
        a package_specification.

        31.b   Additional check names are added.  We allow implementations to
        define their own checks.

                         Wording Changes From Ada 83

        31.c   We define the checks in a distributed manner.  Therefore, the
        long list of what checks apply to what is merely a NOTE.

        31.d   We have removed the detailed rules about what is allowed in a
        pragma Suppress, and allow implementations to invent their own.  The
        RM83 rules weren't quite right, and such a change is necessary anyway
        in the presence of implementation-defined checks.

        31.e   We make it clear that the difference between a Range_Check and
        an Overflow_Check is fuzzy.  This was true in Ada 83, given
        RM83-11.6, but it was not clear.  We considered removing Overflow_
        Check from the language or making it obsolescent, just as we did for
        Numeric_Error.  However, we kept it for upward compatibility, and
        because it may be useful on machines where range checking costs more
        than overflow checking, but overflow checking still costs something.
        Different compilers will suppress different checks when asked to
        suppress Overflow_Check -- the non-uniformity in this case is not
        harmful, and removing it would have a serious impact on optimizers.

        31.f   Under Access_Check, dereferences cover the cases of selected_
        component, indexed_component, slice, and attribute that are listed in
        RM83, as well as the new explicit_dereference, which was included in
        selected_component in RM83.



11.6 Exceptions and Optimization

1   [{language-defined check} {check (language-defined)} {run-time error}
{error (run-time)} {optimization} {efficiency} This clause gives permission
to the implementation to perform certain ``optimizations'' that do not
necessarily preserve the canonical semantics.]


                              Dynamic Semantics

2   {canonical semantics} The rest of this International Standard (outside
this clause) defines the canonical semantics of the language.  [The canonical
semantics of a given (legal) program determines a set of possible external
effects that can result from the execution of the program with given inputs.]

        2.a   Ramification:  Note that the canonical semantics is a set of
        possible behaviors, since some reordering, parallelism, and
        non-determinism is allowed by the canonical semantics.

        2.b   Discussion:  The following parts of the canonical semantics are
        of particular interest to the reader of this clause:

          2.c  Behavior in the presence of abnormal objects and objects
               with invalid representations (see 13.9.1).

          2.d  Various actions that are defined to occur in an arbitrary
               order.

          2.e  Behavior in the presence of a misuse of Unchecked_
               Deallocation, Unchecked_Access, or imported or exported
               entity (see Section 13).

3   [As explained in 1.1.3, ``Conformity of an Implementation With the
Standard'', the external effect of a program is defined in terms of its
interactions with its external environment.  Hence, the implementation can
perform any internal actions whatsoever, in any order or in parallel, so long
as the external effect of the execution of the program is one that is allowed
by the canonical semantics, or by the rules of this clause.]

        3.a   Ramification:  Note that an optimization can change the
        external effect of the program, so long as the changed external
        effect is an external effect that is allowed by the semantics.  Note
        that the canonical semantics of an erroneous execution allows any
        external effect whatsoever.  Hence, if the implementation can prove
        that program execution will be erroneous in certain circumstances,
        there need not be any constraints on the machine code executed in
        those circumstances.


                         Implementation Permissions

4   The following additional permissions are granted to the implementation:

    5  {extra permission to avoid raising exceptions} {undefined result}
       An implementation need not always raise an exception when a
       language-defined check fails.  Instead, the operation that failed
       the check can simply yield an undefined result.  The exception
       need be raised by the implementation only if, in the absence of
       raising it, the value of this undefined result would have some
       effect on the external interactions of the program.  In
       determining this, the implementation shall not presume that an
       undefined result has a value that belongs to its subtype, nor
       even to the base range of its type, if scalar.  [Having removed
       the raise of the exception, the canonical semantics will in
       general allow the implementation to omit the code for the check,
       and some or all of the operation itself.]

 5.a    Ramification:  Even without this permission, an implementation
        can always remove a check if it cannot possibly fail.

 5.b    Reason:  We express the permission in terms of removing the
        raise, rather than the operation or the check, as it minimizes
        the disturbance to the canonical semantics (thereby simplifying
        reasoning).  By allowing the implementation to omit the raise,
        it thereby does not need to "look" at what happens in the
        exception handler to decide whether the optimization is allowed.

 5.c    Discussion:  The implementation can also omit checks if they
        cannot possibly fail, or if they could only fail in erroneous
        executions.  This follows from the canonical semantics.

 5.d    Implementation Note:  This permission is intended to allow
        normal "dead code removal" optimizations, even if some of the
        removed code might have failed some language-defined check.
        However, one may not eliminate the raise of an exception if
        subsequent code presumes in some way that the check succeeded.
        For example:

5.e           if X * Y > Integer'Last then
                  Put_Line("X * Y overflowed");
              end if;
            exception
              when others =>
                  Put_Line("X * Y overflowed");

        If X*Y does overflow, you may not remove the raise of the
        exception if the code that does the comparison against
        Integer'Last presumes that it is comparing it with an in-range
        Integer value, and hence always yields False.

 5.f    As another example where a raise may not be eliminated:

5.g           subtype Str10 is String(1..10);
              type P10 is access Str10;
              X : P10 := null;
            begin
              if X.all'Last = 10 then
                  Put_Line("Oops");
              end if;

        In the above code, it would be wrong to eliminate the raise of
        Constraint_Error on the "X.all" (since X is null), if the code
        to evaluate 'Last always yields 10 by presuming that X.all
        belongs to the subtype Str10, without even "looking."

    6  {extra permission to reorder actions} If an exception is raised
       due to the failure of a language-defined check, then upon
       reaching the corresponding exception_handler (or the termination
       of the task, if none), the external interactions that have
       occurred need reflect only that the exception was raised
       somewhere within the execution of the sequence_of_statements with
       the handler (or the task_body), possibly earlier (or later if the
       interactions are independent of the result of the checked
       operation) than that defined by the canonical semantics, but not
       within the execution of some abort-deferred operation or
       independent subprogram that does not dynamically enclose the
       execution of the construct whose check failed.  {independent
       subprogram} An independent subprogram is one that is defined
       outside the library unit containing the construct whose check
       failed, and has no Inline pragma applied to it.  {normal state of
       an object} {abnormal state of an object [partial]} {disruption of
       an assignment [partial]} Any assignment that occurred outside of
       such abort-deferred operations or independent subprograms can be
       disrupted by the raising of the exception, causing the object or
       its parts to become abnormal, and certain subsequent uses of the
       object to be erroneous, as explained in 13.9.1.

 6.a    Reason:  We allow such variables to become abnormal so that
        assignments (other than to atomic variables) can be disrupted
        due to ``imprecise'' exceptions or instruction scheduling, and
        so that assignments can be reordered so long as the correct
        results are produced in the end if no language-defined checks
        fail.

 6.b    Ramification:  If a check fails, no result dependent on the
        check may be incorporated in an external interaction.  In other
        words, there is no permission to output meaningless results due
        to postponing a check.

        6.c   Discussion:  We believe it is important to state the extra
        permission to reorder actions in terms of what the programmer can
        expect at run time, rather than in terms of what the implementation
        can assume, or what transformations the implementation can perform.
        Otherwise, how can the programmer write reliable programs?

        6.d   This clause has two conflicting goals:  to allow as much
        optimization as possible, and to make program execution as
        predictable as possible (to ease the writing of reliable programs).
        The rules given above represent a compromise.

        6.e   Consider the two extremes:

        6.f   The extreme conservative rule would be to delete this clause
        entirely.  The semantics of Ada would be the canonical semantics.
        This achieves the best predictability.  It sounds like a disaster
        from the efficiency point of view, but in practice, implementations
        would provide modes in which less predictability but more efficiency
        would be achieved.  Such a mode could even be the out-of-the-box
        mode.  In practice, implementers would provide a compromise based on
        their customer's needs.  Therefore, we view this as one viable
        alternative.

        6.g   The extreme liberal rule would be ``the language does not
        specify the execution of a program once a language-defined check has
        failed; such execution can be unpredictable.''  This achieves the
        best efficiency.  It sounds like a disaster from the predictability
        point of view, but in practice it might not be so bad.  A user would
        have to assume that exception handlers for exceptions raised by
        language-defined checks are not portable.  They would have to isolate
        such code (like all nonportable code), and would have to find out,
        for each implementation of interest, what behaviors can be expected.
        In practice, implementations would tend to avoid going so far as to
        punish their customers too much in terms of predictability.

        6.h   The most important thing about this clause is that users
        understand what they can expect at run time, and implementers
        understand what optimizations are allowed.  Any solution that makes
        this clause contain rules that can interpreted in more than one way
        is unacceptable.

        6.i   We have chosen a compromise between the extreme conservative
        and extreme liberal rules.  The current rule essentially allows
        arbitrary optimizations within a library unit and inlined subprograms
        reachable from it, but disallow semantics-disrupting optimizations
        across library units in the absence of inlined subprograms.  This
        allows a library unit to be debugged, and then reused with some
        confidence that the abstraction it manages cannot be broken by bugs
        outside the library unit.


     NOTES
7    (3) The permissions granted by this clause can have an effect on the
     semantics of a program only if the program fails a language-defined
     check.


                         Wording Changes From Ada 83

        7.a   RM83-11.6 was unclear.  It has been completely rewritten here;
        we hope this version is clearer.  Here's what happened to each
        paragraph of RM83-11.6:

          7.b  Paragraphs 1 and 2 contain no semantics; they are merely
               pointing out that anything goes if the canonical
               semantics is preserved.  We have similar introductory
               paragraphs, but we have tried to clarify that these are
               not granting any ``extra'' permission beyond what the
               rest of the document allows.

          7.c  Paragraphs 3 and 4 are reflected in the ``extra
               permission to reorder actions''.  Note that this
               permission now allows the reordering of assignments in
               many cases.

          7.d  Paragraph 5 is moved to 4.5, ``Operators and Expression
               Evaluation'', where operator association is discussed.
               Hence, this is no longer an ``extra permission'' but is
               part of the canonical semantics.

          7.e  Paragraph 6 now follows from the general permission to
               store out-of-range values for unconstrained subtypes.
               Note that the parameters and results of all the
               predefined operators of a type are of the unconstrained
               subtype of the type.

          7.f  Paragraph 7 is reflected in the ``extra permission to
               avoid raising exceptions''.

        7.g   We moved clause 11.5, ``Suppressing Checks'' from after 11.6 to
        before 11.6, in order to preserve the famous number ``11.6'' (given
        the changes to earlier clauses in Section 11).



                          Section 12: Generic Units


1   {generic unit} A generic unit is a program unit that is either a generic
subprogram or a generic package.  {template} A generic unit is a template[,
which can be parameterized, and from which corresponding (nongeneric)
subprograms or packages can be obtained].  The resulting program units are
said to be instances of the original generic unit.  {template: see generic
unit} {macro: see generic unit} {parameter: see generic formal parameter}

        1.a   Glossary entry:  {Generic unit} A generic unit is a template
        for a (nongeneric) program unit; the template can be parameterized by
        objects, types, subprograms, and packages.  An instance of a generic
        unit is created by a generic_instantiation.  The rules of the
        language are enforced when a generic unit is compiled, using a
        generic contract model; additional checks are performed upon
        instantiation to verify the contract is met.  That is, the
        declaration of a generic unit represents a contract between the body
        of the generic and instances of the generic.  Generic units can be
        used to perform the role that macros sometimed play in other
        languages.

2   [A generic unit is declared by a generic_declaration.  This form of
declaration has a generic_formal_part declaring any generic formal
parameters.  An instance of a generic unit is obtained as the result of a
generic_instantiation with appropriate generic actual parameters for the
generic formal parameters.  An instance of a generic subprogram is a
subprogram.  An instance of a generic package is a package.

3   Generic units are templates.  As templates they do not have the
properties that are specific to their nongeneric counterparts.  For example,
a generic subprogram can be instantiated but it cannot be called.  In
contrast, an instance of a generic subprogram is a (nongeneric) subprogram;
hence, this instance can be called but it cannot be used to produce further
instances.]



12.1 Generic Declarations

1   [A generic_declaration declares a generic unit, which is either a generic
subprogram or a generic package.  A generic_declaration includes a generic_
formal_part declaring any generic formal parameters.  A generic formal
parameter can be an object; alternatively (unlike a parameter of a
subprogram), it can be a type, a subprogram, or a package.]


                                   Syntax

2   generic_declaration ::= generic_subprogram_declaration | generic_package_de\
claration

3   generic_subprogram_declaration ::=
         generic_formal_part  subprogram_specification;

4   generic_package_declaration ::=
         generic_formal_part  package_specification;

5   generic_formal_part ::= generic {generic_formal_parameter_declaration | use\
_clause}

6   generic_formal_parameter_declaration ::=
          formal_object_declaration
        | formal_type_declaration
        | formal_subprogram_declaration
        | formal_package_declaration
    7   The only form of subtype_indication allowed within a generic_formal_
    part is a subtype_mark [(that is, the subtype_indication shall not
    include an explicit constraint)].  The defining name of a generic
    subprogram shall be an identifier [(not an operator_symbol)].

        7.a   Reason:  The reason for forbidding constraints in subtype_
        indications is that it simplifies the elaboration of generic_
        declarations (since there is nothing to evaluate), and that it
        simplifies the matching rules, and makes them more checkable at
        compile time.


                              Static Semantics

8   {generic package} {generic subprogram} {generic procedure} {generic
function} A generic_declaration declares a generic unit -- a generic package,
generic procedure or generic function, as appropriate.

9   {generic formal} An entity is a generic formal entity if it is declared
by a generic_formal_parameter_declaration.  ``Generic formal,'' or simply
``formal,'' is used as a prefix in referring to objects, subtypes (and
types), functions, procedures and packages, that are generic formal entities,
as well as to their respective declarations.  [Examples: ``generic formal
procedure'' or a ``formal integer type declaration.'']


                              Dynamic Semantics

10   {elaboration [generic_declaration]} The elaboration of a generic_
declaration has no effect.


     NOTES
11   (1) Outside a generic unit a name that denotes the generic_declaration
     denotes the generic unit.  In contrast, within the declarative region of
     the generic unit, a name that denotes the generic_declaration denotes
     the current instance.

   11.a   Proof:  This is stated officially as part of the ``current
        instance'' rule in 8.6, ``The Context of Overload Resolution''.  See
        also 12.3, ``Generic Instantiation''.

12   (2) Within a generic subprogram_body, the name of this program unit acts
     as the name of a subprogram.  Hence this name can be overloaded, and it
     can appear in a recursive call of the current instance.  For the same
     reason, this name cannot appear after the reserved word new in a
     (recursive) generic_instantiation.

13   (3) A default_expression or default_name appearing in a generic_formal_
     part is not evaluated during elaboration of the generic_formal_part;
     instead, it is evaluated when used.  (The usual visibility rules apply
     to any name used in a default:  the denoted declaration therefore has to
     be visible at the place of the expression.)


                                  Examples

14   Examples of generic formal parts:

15  generic     --  parameterless

16  generic
       Size : Natural;  --  formal object

17  generic
       Length : Integer := 200;          -- formal object with a default expres\
sion

18     Area   : Integer := Length*Length; -- formal object with a default expre\
ssion

19  generic
       type Item  is private;                       -- formal type
       type Index is (<>);                          -- formal type
       type Row   is array(Index range <>) of Item; -- formal type
       with function "<"(X, Y : Item) return Boolean;    -- formal subprogram

20   Examples of generic declarations declaring generic subprograms Exchange
and Squaring:

21  generic
       type Elem is private;
    procedure Exchange(U, V : in out Elem);

22  generic
       type Item is private;
       with function "*"(U, V : Item) return Item is <>;
    function Squaring(X : Item) return Item;

23   Example of a generic declaration declaring a generic package:

24  generic
       type Item   is private;
       type Vector is array (Positive range <>) of Item;
       with function Sum(X, Y : Item) return Item;
    package On_Vectors is
       function Sum  (A, B : Vector) return Vector;
       function Sigma(A    : Vector) return Item;
       Length_Error : exception;
    end On_Vectors;


                            Extensions to Ada 83

        24.a   {extensions to Ada 83} The syntax rule for generic_formal_
        parameter_declaration is modified to allow the reserved words tagged
        and abstract, to allow formal derived types, and to allow formal
        packages.

        24.b   Use_clauses are allowed in generic_formal_parts.  This is
        necessary in order to allow a use_clause within a formal part to
        provide direct visibility of declarations within a generic formal
        package.

                         Wording Changes From Ada 83

        24.c   The syntax for generic_formal_parameter_declaration and
        formal_type_definition is split up into more named categories.  The
        rules for these categories are moved to the appropriate clauses and
        subclauses.  The names of the categories are changed to be more
        intuitive and uniform.  For example, we changed generic_parameter_
        declaration to generic_formal_parameter_declaration, because the
        thing it declares is a generic formal, not a generic.  In the others,
        we abbreviate ``generic_formal'' to just ``formal''.  We can't do
        that for generic_formal_parameter_declaration, because of confusion
        with normal formal parameters of subprograms.



12.2 Generic Bodies

1   {generic body} The body of a generic unit (a generic body) [is a template
for the instance bodies.  The syntax of a generic body is identical to that
of a nongeneric body].

        1.a   Ramification:  We also use terms like ``generic function body''
        and ``nongeneric package body.''


                              Dynamic Semantics

2   {elaboration [generic body]} The elaboration of a generic body has no
other effect than to establish that the generic unit can from then on be
instantiated without failing the Elaboration_Check.  If the generic body is a
child of a generic package, then its elaboration establishes that each
corresponding declaration nested in an instance of the parent (see 10.1.1)
can from then on be instantiated without failing the Elaboration_Check.
{94-4933.a}


     NOTES
3    (4) The syntax of generic subprograms implies that a generic subprogram
     body is always the completion of a declaration.


                                  Examples

4   Example of a generic procedure body:

5   procedure Exchange(U, V : in out Elem) is  -- see 12.1
       T : Elem;  --  the generic formal type
    begin
       T := U;
       U := V;
       V := T;
    end Exchange;

6   Example of a generic function body:

7   function Squaring(X : Item) return Item is  --  see 12.1
    begin
       return X*X;  --  the formal operator "*"
    end Squaring;

8   Example of a generic package body:

9   package body On_Vectors is  --  see 12.1

10     function Sum(A, B : Vector) return Vector is
          Result : Vector(A'Range); --  the formal type Vector
          Bias   : constant Integer := B'First - A'First;
       begin
          if A'Length /= B'Length then
             raise Length_Error;
          end if;

11        for N in A'Range loop
             Result(N) := Sum(A(N), B(N + Bias)); -- the formal function Sum
          end loop;
          return Result;
       end Sum;

12     function Sigma(A : Vector) return Item is
          Total : Item := A(A'First); --  the formal type Item
       begin
          for N in A'First + 1 .. A'Last loop
             Total := Sum(Total, A(N)); --  the formal function Sum
          end loop;
          return Total;
       end Sigma;
    end On_Vectors;
12.3 Generic Instantiation

1   [{instance (of a generic unit)} An instance of a generic unit is declared
by a generic_instantiation.]


                         Language Design Principles

        1.a   {generic contract model} {contract model of generics} The
        legality of an instance should be determinable without looking at the
        generic body.  Likewise, the legality of a generic body should be
        determinable without looking at any instances.  Thus, the generic_
        declaration forms a contract between the body and the instances; if
        each obeys the rules with respect to the generic_declaration, then no
        legality problems will arise.  This is really a special case of the
        ``legality determinable via semantic dependences'' Language Design
        Principle (see Section 10), given that a generic_instantiation does
        not depend semantically upon the generic body, nor vice-versa.

        1.b   Run-time issues are another story.  For example, whether
        parameter passing is by copy or by reference is determined in part by
        the properties of the generic actuals, and thus cannot be determined
        at compile time of the generic body.  Similarly, the contract model
        does not apply to Post-Compilation Rules.

                                   Syntax

2   generic_instantiation ::=
         package defining_program_unit_name is
             new generic_package_name [generic_actual_part];
       | procedure defining_program_unit_name is
             new generic_procedure_name [generic_actual_part];
       | function defining_designator is
             new generic_function_name [generic_actual_part];

3   generic_actual_part ::=
       (generic_association {, generic_association})

4   generic_association ::=
       [generic_formal_parameter_selector_name =>] explicit_generic_actual_para\
meter

5   explicit_generic_actual_parameter ::= expression | variable_name
       | subprogram_name | entry_name | subtype_mark
       | package_instance_name

    6   {named association} {positional association} A generic_association is
    named or positional according to whether or not the generic_formal_
    parameter_selector_name is specified.  Any positional associations shall
    precede any named associations.


7   {generic actual parameter} {generic actual} {actual} The generic actual
parameter is either the explicit_generic_actual_parameter given in a generic_
parameter_association for each formal, or the corresponding default_
expression or default_name if no generic_parameter_association is given for
the formal.  When the meaning is clear from context, the term ``generic
actual,'' or simply ``actual,'' is used as a synonym for ``generic actual
parameter'' and also for the view denoted by one, or the value of one.


                               Legality Rules

8   In a generic_instantiation for a particular kind of program unit
[(package, procedure, or function)], the name shall denote a generic unit of
the corresponding kind [(generic package, generic procedure, or generic
function, respectively)].

9   The generic_formal_parameter_selector_name of a generic_association shall
denote a generic_formal_parameter_declaration of the generic unit being
instantiated.  If two or more formal subprograms have the same defining name,
then named associations are not allowed for the corresponding actuals.

10   A generic_instantiation shall contain at most one generic_association
for each formal.  Each formal without an association shall have a default_
expression or subprogram_default.

11   In a generic unit Legality Rules are enforced at compile time of the
generic_declaration and generic body, given the properties of the formals.
In the visible part and formal part of an instance, Legality Rules are
enforced at compile time of the generic_instantiation, given the properties
of the actuals.  {94-4804.a} {94-4808.a} In other parts of an instance,
Legality Rules are not enforced; this rule does not apply when a given rule
explicitly specifies otherwise.

        11.a   Reason:  Since rules are checked using the properties of the
        formals, and since these properties do not always carry over to the
        actuals, we need to check the rules again in the visible part of the
        instance.  For example, only if a tagged type is limited may an
        extension of it have limited components in the extension_part.  A
        formal tagged limited type is limited, but the actual might be
        nonlimited.  Hence any rule that requires a tagged type to be limited
        runs into this problem.  Such rules are rare; in most cases, the
        rules for matching of formals and actuals guarantee that if the rule
        is obeyed in the generic unit, then it has to be obeyed in the
        instance.

        11.b   Ramification:  The ``properties'' of the formals are
        determined without knowing anything about the actuals:

         11.c  A formal derived subtype is constrained if and only if
               the ancestor subtype is constrained.  A formal array type
               is constrained if and only if the declarations says so.
               Other formal subtypes are unconstrained, even though they
               might be constrained in an instance.

         11.d  A formal subtype can be indefinite, even though the copy
               might be definite in an instance.

         11.e  A formal object of mode in is not a static constant; in
               an instance, the copy is static if the actual is.

         11.f  A formal subtype is not static, even though the actual
               might be.

         11.g  Formal types are specific, even though the actual can be
               class-wide.

         11.h  The subtype of a formal object of mode in out is not
               static.  (This covers the case of AI-00878.)

         11.i  The subtype of a formal parameter of a formal subprogram
               does not provide an applicable index constraint.

         11.j  The profile of a formal subprogram is not subtype-
               conformant with any other profile.  {subtype conformance}
               {94-4774.b}

         11.k  A generic formal function is not static.

        11.l   Ramification:  The exceptions to the above rule about when
        legality rules are enforced fall into these categories:

         11.m  Some rules are checked in the generic declaration, and
               then again in both the visible and private parts of the
               instance:

                11.n  The parent type of a record extension has to be
                      specific (see 3.9.1).  This rule is not checked in
                      the instance body.

                11.o  The parent type of a private extension has to be
                      specific (see 7.3).  This rule is not checked in
                      the instance body.

                11.p  A type with an access discriminant has to be a
                      descendant of a type declared with limited, or be
                      a task or protected type.  This rule is irrelevant
                      in the instance body.

                11.q  In the declaration of a record extension, if the
                      parent type is nonlimited, then each of the
                      components of the record_extension_part have to be
                      nonlimited (see 3.9.1).  In the generic body, this
                      rule is checked in an assume-the-worst manner.

                11.r  A preelaborated library unit has to be
                      preelaborable (see 10.2.1).  In the generic body,
                      this rule is checked in an assume-the-worst
                      manner.

         11.s  {accessibility rule [checking in generic units]} For the
               accessibility rules, the formals have nothing to say
               about the property in question.  Like the above rules,
               these rules are checked in the generic declaration, and
               then again in both the visible and private parts of the
               instance.  In the generic body, we have explicit rules
               that essentially assume the worst (in the cases of type
               extensions and access-to-subprogram types), and we have
               run-time checks (in the case of access-to-object types).
               See 3.9.1, 3.10.2, and 4.6.

               11.t   We considered run-time checks for access-to-
               subprogram types as well.  However, this would present
               difficulties for implementations that share generic
               bodies.

         11.u  The rules requiring ``reasonable'' values for static
               expressions are ignored when the expected type for the
               expression is a descendant of a generic formal type other
               than a generic formal derived type, and do not apply in
               an instance.

         11.v  The rule forbidding two explicit homographs in the same
               declarative region does not apply in an instance of a
               generic unit, except that it does apply in the
               declaration of a record extension that appears in the
               visible part of an instance.

         11.w  Some rules do not apply at all in an instance, not even
               in the visible part:

                11.x  Body_stubs are not normally allowed to be multiply
                      nested, but the can be in instances.

        11.y   {generic contract issue [distributed]} Each rule that is an
        exception is marked with ``generic contract issue;'' look that up in
        the index to find them all.

        11.z   Ramification:  The Legality Rules are the ones labeled
        Legality Rules.  We are talking about all Legality Rules in the
        entire language here.  Note that, with some exceptions, the legality
        of a generic unit is checked even if there are no instantiations of
        the generic unit.

        11.aa   Ramification:  The Legality Rules are described here, and the
        overloading rules were described earlier in this clause.  Presumably,
        every Static Semantic Item is sucked in by one of those.  Thus, we
        have covered all the compile-time rules of the language.  There is no
        need to say anything special about the Post-Compilation Rules or the
        Dynamic Semantic Items.

        11.bb   Discussion:  Here is an example illustrating how this rule is
        checked:  ``In the declaration of a record extension, if the parent
        type is nonlimited, then each of the components of the record_
        extension_part shall be nonlimited.''

11.cc       generic
                type Parent is tagged private;
                type Comp is limited private;
            package G1 is
                type Extension is new Parent with
                    record
                        C : Comp; -- Illegal!
                    end record;
            end G1;

        11.dd   The parent type is nonlimited, and the component type is
        limited, which is illegal.  It doesn't matter that an one could
        imagine writing an instantiation with the actual for Comp being
        nonlimited -- we never get to the instance, because the generic
        itself is illegal.

        11.ee   On the other hand:

11.ff       generic
                type Parent is tagged limited private; -- Parent is limited.
                type Comp is limited private;
            package G2 is
                type Extension is new Parent with
                    record
                        C : Comp; -- OK.
                    end record;
            end G2;

11.gg       type Limited_Tagged is tagged limited null record;
            type Non_Limited_Tagged is tagged null record;

11.hh       type Limited_Untagged is limited null record;
            type Non_Limited_Untagged is null record;

11.ii       package Good_1 is new G2(Parent => Limited_Tagged,
                                     Comp => Limited_Untagged);
            package Good_2 is new G2(Parent => Non_Limited_Tagged,
                                     Comp => Non_Limited_Untagged);
            package Bad  is new G2(Parent => Non_Limited_Tagged,
                                     Comp => Limited_Untagged); -- Illegal!

        11.jj   The first instantiation is legal, because in the instance the
        parent is limited, so the rule is not violated.  Likewise, in the
        second instantiation, the rule is not violated in the instance.
        However, in the Bad instance, the parent type is nonlimited, and the
        component type is limited, so this instantiation is illegal.


                              Static Semantics

12   A generic_instantiation declares an instance; it is equivalent to the
instance declaration (a package_declaration or subprogram_declaration)
immediately followed by the instance body, both at the place of the
instantiation.

        12.a   Ramification:  The declaration and the body of the instance
        are not ``implicit'' in the technical sense, even though you can't
        see them in the program text.  Nor are declarations within an
        instance ``implicit'' (unless they are implicit by other rules).
        This is necessary because implicit declarations have special
        semantics that should not be attached to instances.  For a generic
        subprogram, the profile of a generic_instantiation is that of the
        instance declaration, by the stated equivalence.

        12.b   Ramification:  {visible part [of an instance]} {private part
        [of a package]} The visible and private parts of a package instance
        are defined in 7.1, ``Package Specifications and Declarations'' and
        12.7, ``Formal Packages''.  The visible and private parts of a
        subprogram instance are defined in 8.2, ``Scope of Declarations''.

13   The instance is a copy of the text of the template.  [Each use of a
formal parameter becomes (in the copy) a use of the actual, as explained
below.]  {package instance} {subprogram instance} {procedure instance}
{function instance} {instance (of a generic package)} {instance (of a generic
subprogram)} {instance (of a generic procedure)} {instance (of a generic
function)} An instance of a generic package is a package, that of a generic
procedure is a procedure, and that of a generic function is a function.

        13.a   Ramification:  An instance is a package or subprogram (because
        we say so), even though it contains a copy of the generic_formal_
        part, and therefore doesn't look like one.  This is strange, but it's
        OK, since the syntax rules are overloading rules, and therefore do
        not apply in an instance.

        13.b   Discussion:  We use a macro-expansion model, with some
        explicitly-stated exceptions (see below).  The main exception is that
        the interpretation of each construct in a generic unit (especially
        including the denotation of each name) is determined when the
        declaration and body of the generic unit (as opposed to the instance)
        are compiled, and in each instance this interpretation is (a copy of)
        the template interpretation.  In other words, if a construct is
        interpreted as a name denoting a declaration D, then in an instance,
        the copy of the construct will still be a name, and will still denote
        D (or a copy of D).  From an implementation point of view, overload
        resolution is performed on the template, and not on each copy.

        13.c   We describe the substitution of generic actual parameters by
        saying (in most cases) that the copy of each generic formal parameter
        declares a view of the actual.  Suppose a name in a generic unit
        denotes a generic_formal_parameter_declaration.  The copy of that
        name in an instance will denote the copy of that generic_formal_
        parameter_declaration in the instance.  Since the generic_formal_
        parameter_declaration in the instance declares a view of the actual,
        the name will denote a view of the actual.

        13.d   Other properties of the copy (for example, staticness, classes
        to which types belong) are recalculated for each instance; this is
        implied by the fact that it's a copy.

        13.e   Although the generic_formal_part is included in an instance,
        the declarations in the generic_formal_part are only visible outside
        the instance in the case of a generic formal package whose formal_
        package_actual_part is (<>) -- see 12.7.

14   The interpretation of each construct within a generic declaration or
body is determined using the overloading rules when that generic declaration
or body is compiled.  In an instance, the interpretation of each (copied)
construct is the same, except in the case of a name that denotes the generic_
declaration or some declaration within the generic unit; the corresponding
name in the instance then denotes the corresponding copy of the denoted
declaration.  The overloading rules do not apply in the instance.

        14.a   Ramification:  See 8.6, ``The Context of Overload Resolution''
        for definitions of ``interpretation'' and ``overloading rule.''

        14.b   Even the generic_formal_parameter_declarations have cor-
        responding declarations in the instance, which declare views of the
        actuals.

        14.c   Although the declarations in the instance are copies of those
        in the generic unit, they often have quite different properties, as
        explained below.  For example a constant declaration in the generic
        unit might declare a nonstatic constant, whereas the copy of that
        declaration might declare a static constant.  This can happen when
        the staticness depends on some generic formal.

        14.d   This rule is partly a ramification of the ``current instance''
        rule in 8.6, ``The Context of Overload Resolution''.  Note that that
        rule doesn't cover the generic_formal_part.

        14.e   Although the overloading rules are not observed in the
        instance, they are, of course, observed in the _instantiation in
        order to determine the interpretation of the constituents of the
        _instantiation.

        14.f   Since children are considered to occur within their parent's
        declarative region, the above rule applies to a name that denotes a
        child of a generic unit, or a declaration inside such a child.

        14.g   Since the Syntax Rules are overloading rules, it is possible
        (legal) to violate them in an instance.  For example, it is possible
        for an instance body to occur in a package_specification, even though
        the Syntax Rules forbid bodies in package_specifications.

15   In an instance, a generic_formal_parameter_declaration declares a view
whose properties are identical to those of the actual, except as specified in
12.4, ``Formal Objects'' and 12.6, ``Formal Subprograms''.  Similarly, for a
declaration within a generic_formal_parameter_declaration, the corresponding
declaration in an instance declares a view whose properties are identical to
the corresponding declaration within the declaration of the actual.

        15.a   Ramification:  In an instance, there are no ``properties'' of
        types and subtypes that come from the formal.  The primitive
        operations of the type come from the formal, but these are
        declarations in their own right, and are therefore handled
        separately.

        15.b   Note that certain properties that come from the actuals are
        irrelevant in the instance.  For example, if an actual type is of a
        class deeper in the derived-type hierarchy than the formal, it is
        impossible to call the additional operations of the deeper class in
        the instance, because any such call would have to be a copy of some
        corresponding call in the generic unit, which would have been
        illegal.  However, it is sometimes possible to reach into the
        specification of the instance from outside, and notice such
        properties.  For example, one could pass an object declared in the
        instance specification to one of the additional operations of the
        deeper type.

        15.c   A formal_type_declaration can contain discriminant_specifica-
        tions, a formal_subprogram_declaration can contain formal_parameter_
        specifications, and a formal_package_declaration can contain many
        kinds of declarations.  These are all inside the generic unit, and
        have corresponding declarations in the instance.

        15.d   This rule implies, for example, that if a subtype in a generic
        unit is a subtype of a generic formal subtype, then the corresponding
        subtype in the instance is a subtype of the corresponding actual
        subtype.

        15.e   For a generic_instantiation, if a generic actual is a static
        [(scalar or string)] subtype, then each use of the corresponding
        formal parameter within the specification of the instance is
        considered to be static.  (See AI-00409.)

        15.f   Similarly, if a generic actual is a static expression and the
        corresponding formal parameter has a static [(scalar or string)]
        subtype, then each use of the formal parameter in the specification
        of the instance is considered to be static.  (See AI-00505.)

        15.g   If a primitive subprogram of a type derived from a generic
        formal derived tagged type is not overriding (that is, it is a new
        subprogram), it is possible for the copy of that subprogram in an
        instance to override a subprogram inherited from the actual.  For
        example:

15.h        type T1 is tagged record ... end record;

15.i        generic
                type Formal is new T1;
            package G is
                type Derived_From_Formal is new Formal with record ... end reco\
rd;
                procedure Foo(X : in Derived_From_Formal); -- Does not override\
 anything.
            end G;

15.j        type T2 is new T1 with record ... end record;
            procedure Foo(X : in T2);

15.k        package Inst is new G(Formal => T2);

        15.l   In the instance Inst, the declaration of Foo for Derived_From_
        Formal overrides the Foo inherited from T2.

        15.m   Implementation Note:  For formal types, an implementation that
        shares the code among multiple instances of the same generic unit
        needs to beware that things like parameter passing mechanisms
        (by-copy vs. by-reference) and representation_clauses are determined
        by the actual.

16   [Implicit declarations are also copied, and a name that denotes an
implicit declaration in the generic denotes the corresponding copy in the
instance.  However, for a type declared within the visible part of the
generic, a whole new set of primitive subprograms is implicitly declared for
use outside the instance, and may differ from the copied set if the
properties of the type in some way depend on the properties of some actual
type specified in the instantiation.  For example, if the type in the generic
is derived from a formal private type, then in the instance the type will
inherit subprograms from the corresponding actual type.

17   {override} These new implicit declarations occur immediately after the
type declaration in the instance, and override the copied ones.  The copied
ones can be called only from within the instance; the new ones can be called
only from outside the instance, although for tagged types, the body of a new
one can be executed by a call to an old one.]

        17.a   Proof:  This rule is stated officially in 8.3, ``Visibility''.

        17.b   Ramification:  The new ones follow from the class(es) of the
        formal types.  For example, for a type T derived from a generic
        formal private type, if the actual is Integer, then the copy of T in
        the instance has a "+" primitive operator, which can be called from
        outside the instance (assuming T is declared in the visible part of
        the instance).

        17.c   AI-00398.

        17.d   Since an actual type is always in the class determined for the
        formal, the new subprograms hide all of the copied ones, except for a
        declaration of "/=" that corresponds to an explicit declaration of
        "=".  Such "/=" operators are special, because unlike other implicit
        declarations of primitive subprograms, they do not appear by virtue
        of the class, but because of an explicit declaration of "=".  If the
        declaration of "=" is implicit (and therefore overridden in the
        instance), then a corresponding implicitly declared "/=" is also
        overridden.  But if the declaration of "=" is explicit (and therefore
        not overridden in the instance), then a corresponding implicitly
        declared "/=" is not overridden either, even though it's implicit.

        17.e   Note that the copied ones can be called from inside the
        instance, even though they are hidden from all visibility, because
        the names are resolved in the generic unit -- visibility is
        irrelevant for calls in the instance.

18   [In the visible part of an instance, an explicit declaration overrides
an implicit declaration if they are homographs, as described in 8.3.]  On the
other hand, an explicit declaration in the private part of an instance
overrides an implicit declaration in the instance, only if the corresponding
explicit declaration in the generic overrides a corresponding implicit
declaration in the generic.  Corresponding rules apply to the other kinds of
overriding described in 8.3.

        18.a   Ramification:  For example:

18.b        type Ancestor is tagged null record;

18.c        generic
                type Formal is new Ancestor with private;
            package G is
                type T is new Formal with null record;
                procedure P(X : in T); -- (1)
            private
                procedure Q(X : in T); -- (2)
            end G;

18.d        type Actual is new Ancestor with null record;
            procedure P(X : in Actual);
            procedure Q(X : in Actual);

18.e        package Instance is new G(Formal => Actual);

        18.f   In the instance, the copy of P at (1) overrides Actual's P,
        whereas the copy of Q at (2) does not override anything; in
        implementation terms, it occupies a separate slot in the type
        descriptor.

        18.g   Reason:  The reason for this rule is so a programmer writing
        an _instantiation need not look at the private part of the generic in
        order to determine which subprograms will be overridden.


                           Post-Compilation Rules

19   {post-compilation rules} Recursive generic instantiation is not allowed
in the following sense: if a given generic unit includes an instantiation of
a second generic unit, then the instance generated by this instantiation
shall not include an instance of the first generic unit [(whether this
instance is generated directly, or indirectly by intermediate
instantiations)].

        19.a   Discussion:  Note that this rule is not a violation of the
        generic contract model, because it is not a Legality Rule.  Some
        implementations may be able to check this rule at compile time, but
        that requires access to all the bodies, so we allow implementations
        to check the rule at link time.


                              Dynamic Semantics

20   {elaboration [generic_instantiation]} For the elaboration of a generic_
instantiation, each generic_association is first evaluated.  If a default is
used, an implicit generic_association is assumed for this rule.  These
evaluations are done in an arbitrary order, except that the evaluation for a
default actual takes place after the evaluation for another actual if the
default includes a name that denotes the other one.  Finally, the instance
declaration and body are elaborated.

        20.a   Ramification:  Note that if the evaluation of a default
        depends on some side-effect of some other evaluation, the order is
        still arbitrary.

21   {evaluation [generic_association]} For the evaluation of a generic_
association the generic actual parameter is evaluated.  Additional actions
are performed in the case of a formal object of mode in (see 12.4).

        21.a   To be honest:  Actually, the actual is evaluated only if
        evaluation is defined for that kind of construct -- we don't actually
        ``evaluate'' subtype_marks.


     NOTES
22   (5) If a formal type is not tagged, then the type is treated as an
     untagged type within the generic body.  Deriving from such a type in a
     generic body is permitted; the new type does not get a new tag value,
     even if the actual is tagged.  Overriding operations for such a derived
     type cannot be dispatched to from outside the instance.

   22.a   Ramification:  If two overloaded subprograms declared in a generic
        package specification differ only by the (formal) type of their
        parameters and results, then there exist legal instantiations for
        which all calls of these subprograms from outside the instance are
        ambiguous.  For example:

22.b        generic
               type A is (<>);
               type B is private;
            package G is
               function Next(X : A) return A;
               function Next(X : B) return B;
            end G;

22.c        package P is new G(A => Boolean, B => Boolean);
            -- All calls of P.Next are ambiguous.

   22.d   Ramification:  The following example illustrates some of the
        subtleties of the substitution of formals and actuals:

22.e        generic
                type T1 is private;
                -- A predefined "=" operator is implicitly declared here:
                -- function "="(Left, Right : T1) return Boolean;
                -- Call this "=" .
                                1
            package G is
                subtype S1 is T1; -- So we can get our hands on the type from
                                  -- outside an instance.
                type T2 is new T1;
                -- An inherited "=" operator is implicitly declared here:
                -- function "="(Left, Right : T2) return Boolean;
                -- Call this "=" .
                                2
22.f            T1_Obj : T1 := ...;
                Bool_1 : Boolean := T1_Obj = T1_Obj;

22.g            T2_Obj : T2 := ...;
                Bool_2 : Boolean := T2_Obj = T2_Obj;
            end G;
            ...

22.h        package P is
                type My_Int is new Integer;
                -- A predefined "=" operator is implicitly declared here:
                -- function "="(Left, Right : My_Int) return Boolean;
                -- Call this "=" .
                                3
                function "="(X, Y : My_Int) return Boolean;
                -- Call this "=" .
                                4
                -- "="  is hidden from all visibility by "=" .
                      3                                     4
                -- Nonetheless, "="  can ``reemerge'' in certain circumstances.
                                   3
            end P;
            use P;
            ...
            package I is new G(T1 => My_Int); -- "="  is declared in I (see bel\
ow).
                                                    5
            use I;

22.i        Another_T1_Obj : S1 := 13; -- Can't denote T1, but S1 will do.
            Bool_3 : Boolean := Another_T1_Obj = Another_T1_Obj;

22.j        Another_T2_Obj : T2 := 45;
            Bool_4 : Boolean := Another_T2_Obj = Another_T2_Obj;

22.k        Double : T2 := T2_Obj + Another_T2_Obj;

   22.l   In the instance I, there is a copy of "="  (call it "="  ) and "="
                                                   1             1i         2
        (call it "="  ).  The "="   and "="   declare views of the predefined
                    2i           1i        2i
        "=" of My_Int (that is, "=" ).  In the initialization of Bool_1 and
                                   3
        Bool_2 in the generic unit G, the names "=" denote "="  and "=" ,
                                                              1        2
        respectively.  Therefore, the copies of these names in the instances
        denote "="   and "="  , respectively.  Thus, the initialization of
                  1i        2i
        I.Bool_1 and I.Bool_2 call the predefined equality operator of My_
        Int; they will not call "=" .
                                   4
   22.m   The declarations "="   and "="   are hidden from all visibility.
                              1i        2i
        This prevents them from being called from outside the instance.

   22.n   The declaration of Bool_3 calls "=" .
                                             4
   22.o   The instance I also contains implicit declarations of the primitive
        operators of T2, such as "=" (call it "=" ) and "+".  These
                                                 5
        operations cannot be called from within the instance, but the
        declaration of Bool_4 calls "=" .
                                       5

                                  Examples

23   Examples of generic instantiations (see 12.1):

24
    procedure Swap is new Exchange(Elem => Integer);
    procedure Swap is new Exchange(Character);  --  Swap is overloaded
    function Square is new Squaring(Integer);   --  "*" of Integer used by defa\
ult
    function Square is new Squaring(Item => Matrix, "*" => Matrix_Product);
    function Square is new Squaring(Matrix, Matrix_Product); -- same as previous

25  package Int_Vectors is new On_Vectors(Integer, Table, "+");

26   Examples of uses of instantiated units:

27  Swap(A, B);
    A := Square(A);

28  T : Table(1 .. 5) := (10, 20, 30, 40, 50);
    N : Integer := Int_Vectors.Sigma(T);  --  150 (see 12.2, ``Generic Bodies''\
 for the body of Sigma)

29  use Int_Vectors;
    M : Integer := Sigma(T);  --  150


                         Inconsistencies With Ada 83

        29.a   {inconsistencies with Ada 83} In Ada 83, all explicit actuals
        are evaluated before all defaults, and the defaults are evaluated in
        the order of the formal declarations.  This ordering requirement is
        relaxed in Ada 9X.

                        Incompatibilities With Ada 83

        29.b   {incompatibilities with Ada 83} We have attempted to remove
        every violation of the contract model.  Any remaining contract model
        violations should be considered bugs in the RM9X.  The unfortunate
        property of reverting to the predefined operators of the actual types
        is retained for upward compatibility.  (Note that fixing this would
        require subtype conformance rules.)  However, tagged types do not
        revert in this sense.

                            Extensions to Ada 83

        29.c   {extensions to Ada 83} The syntax rule for explicit_generic_
        actual_parameter is modified to allow a package_instance_name.

                         Wording Changes From Ada 83

        29.d   The fact that named associations cannot be used for two formal
        subprograms with the same defining name is moved to AARM-only
        material, because it is a ramification of other rules, and because it
        is not of interest to the average user.

        29.e   The rule that ``An explicit explicit_generic_actual_parameter
        shall not be supplied more than once for a given generic_formal_
        parameter'' seems to be missing from RM83, although it was clearly
        the intent.

        29.f   In the explanation that the instance is a copy of the
        template, we have left out RM83-12.3(5)'s ``apart from the generic
        formal part'', because it seems that things in the formal part still
        need to exist in instances.  This is particularly true for generic
        formal packages, where you're sometimes allowed to reach in and
        denote the formals of the formal package from outside it.  This
        simplifies the explanation of what each name in an instance denotes:
        there are just two cases: the declaration can be inside or outside
        (where inside needs to include the generic unit itself).  Note that
        the RM83 approach of listing many cases (see RM83-12.5(5-14)) would
        have become even more unwieldy with the addition of generic formal
        packages, and the declarations that occur therein.

        29.g   We have corrected the definition of the elaboration of a
        generic_instantiation (RM83-12.3(17)); we don't elaborate entities,
        and the instance is not ``implicit.''

        29.h   In RM83, there is a rule saying the formal and actual shall
        match, and then there is much text defining what it means to match.
        Here, we simply state all the latter text as rules.  For example, ``A
        formal foo is matched by an actual greenish bar'' becomes ``For a
        formal foo, the actual shall be a greenish bar.''  This is necessary
        to split the Name Resolution Rules from the Legality Rules.  Besides,
        there's really no need to define the concept of matching for generic
        parameters.



12.4 Formal Objects

1   [{generic formal object} {formal object, generic} A generic formal object
can be used to pass a value or variable to a generic unit.]


                         Language Design Principles

        1.a   A generic formal object of mode in is like a constant
        initialized to the value of the explicit_generic_actual_parameter.

        1.b   A generic formal object of mode in out is like a renaming of
        the explicit_generic_actual_parameter.

                                   Syntax

2   formal_object_declaration ::=
        defining_identifier_list : mode subtype_mark [:= default_expression];


                            Name Resolution Rules

3   {expected type [generic formal object default_expression]} The expected
type for the default_expression, if any, of a formal object is the type of
the formal object.

4   {expected type [generic formal in object actual]} For a generic formal
object of mode in, the expected type for the actual is the type of the
formal.

5   For a generic formal object of mode in out, the type of the actual shall
resolve to the type of the formal.  {94-4500.a} {94-4505.a} {94-4506.a}
{94-4507.a} {94-4509.a} {94-4532.a}

        5.a   Reason:  See the corresponding rule for object_renaming_
        declarations for a discussion of the reason for this rule.


                               Legality Rules

6   If a generic formal object has a default_expression, then the mode shall
be in [(either explicitly or by default)]; otherwise, its mode shall be
either in or in out.
        6.a   Ramification:  Mode out is not allowed for generic formal
        objects.

7   For a generic formal object of mode in, the actual shall be an
expression.  For a generic formal object of mode in out, the actual shall be
a name that denotes a variable for which renaming is allowed (see 8.5.1).

        7.a   To be honest:  The part of this that requires an expression or
        name is a Name Resolution Rule, but that's too pedantic to worry
        about.  (The part about denoting a variable, and renaming being
        allowed, is most certainly not a Name Resolution Rule.)

8   The type of a generic formal object of mode in shall be nonlimited.

        8.a   Reason:  Since a generic formal object is like a constant of
        mode in initialized to the value of the actual, a limited type would
        not make sense, since initializing a constant is not allowed for a
        limited type.  That is, generic formal objects of mode in are passed
        by copy, and limited types are not supposed to be copied.


                              Static Semantics

9   A formal_object_declaration declares a generic formal object.  The
default mode is in.  {nominal subtype [of a generic formal object]} For a
formal object of mode in, the nominal subtype is the one denoted by the
subtype_mark in the declaration of the formal.  {static [subtype]} For a
formal object of mode in out, its type is determined by the subtype_mark in
the declaration; its nominal subtype is nonstatic, even if the subtype_mark
denotes a static subtype.

10   {stand-alone constant (corresponding to a formal object of mode in)} In
an instance, a formal_object_declaration of mode in declares a new
stand-alone constant object whose initialization expression is the actual,
whereas a formal_object_declaration of mode in out declares a view whose
properties are identical to those of the actual.

        10.a   Ramification:  These rules imply that generic formal objects
        of mode in are passed by copy, whereas generic formal objects of mode
        in out are passed by reference.

        10.b   Initialization and finalization happen for the constant
        declared by a formal_object_declaration of mode in as for any
        constant; see 3.3.1, ``Object Declarations'' and 7.6, ``User-Defined
        Assignment and Finalization''.

        10.c   {subtype [of a generic formal object]} In an instance, the
        subtype of a generic formal object of mode in is as for the
        equivalent constant.  In an instance, the subtype of a generic formal
        object of mode in out is the subtype of the corresponding generic
        actual.


                              Dynamic Semantics

11   {evaluation [generic_association for a formal object of mode in]}
{assignment operation (during evaluation of a generic_association for a
formal object of mode in)} For the evaluation of a generic_association for a
formal object of mode in, a constant object is created, the value of the
actual parameter is converted to the nominal subtype of the formal object,
and assigned to the object[, including any value adjustment -- see 7.6].
{implicit subtype conversion [generic formal object of mode in]}

        11.a   Ramification:  This includes evaluating the actual and doing a
        subtype conversion, which might raise an exception.

        11.b   Discussion:  The rule for evaluating a generic_association for
        a formal object of mode in out is covered by the general Dynamic
        Semantics rule in 12.3.


     NOTES
12   (6) The constraints that apply to a generic formal object of mode in out
     are those of the corresponding generic actual parameter (not those
     implied by the subtype_mark that appears in the formal_object_
     declaration).  Therefore, to avoid confusion, it is recommended that the
     name of a first subtype be used for the declaration of such a formal
     object.

   12.a   Ramification:  Constraint checks are done at instantiation time for
        formal objects of mode in, but not for formal objects of mode in out.


                            Extensions to Ada 83

        12.b   {extensions to Ada 83} In Ada 83, it is forbidden to pass a
        (nongeneric) formal parameter of mode out, or a subcomponent thereof,
        to a generic formal object of mode in out.  This restriction is
        removed in Ada 9X.

                         Wording Changes From Ada 83

        12.c   We make ``mode'' explicit in the syntax.  RM83 refers to the
        mode without saying what it is.  This is also more uniform with the
        way (nongeneric) formal parameters are defined.

        12.d   We considered allowing mode out in Ada 9X, for uniformity with
        (nongeneric) formal parameters.  The semantics would be identical for
        modes in out and out.  (Note that generic formal objects of mode in
        out are passed by reference.  Note that for (nongeneric) formal
        parameters that are allowed to be passed by reference, the semantics
        of in out and out is the same.  The difference might serve as
        documentation.  The same would be true for generic formal objects, if
        out were allowed, so it would be consistent.)  We decided not to make
        this change, because it does not produce any important benefit, and
        any change has some cost.



12.5 Formal Types

1   [A generic formal subtype can be used to pass to a generic unit a subtype
whose type is in a certain class of types.]

        1.a   Reason:  We considered having intermediate syntactic categories
        formal_integer_type_definition, formal_real_type_definition, and
        formal_fixed_point_definition, to be more uniform with the syntax
        rules for non-generic-formal types.  However, that would make the
        rules for formal types slightly more complicated, and it would cause
        confusion, since formal_discrete_type_definition would not fit into
        the scheme very well.


                                   Syntax

2   formal_type_declaration ::=
        type defining_identifier[discriminant_part] is formal_type_definition;

3   formal_type_definition ::=
          formal_private_type_definition
        | formal_derived_type_definition
        | formal_discrete_type_definition
        | formal_signed_integer_type_definition
        | formal_modular_type_definition
        | formal_floating_point_definition
        | formal_ordinary_fixed_point_definition
        | formal_decimal_fixed_point_definition
        | formal_array_type_definition
        | formal_access_type_definition


                               Legality Rules

4   {generic actual subtype} {actual subtype} {generic actual type} {actual
type} For a generic formal subtype, the actual shall be a subtype_mark; it
denotes the (generic) actual subtype.

        4.a   Ramification:  When we say simply ``formal'' or ``actual'' (for
        a generic formal that denotes a subtype) we're talking about the
        subtype, not the type, since a name that denotes a formal_type_
        declaration denotes a subtype, and the corresponding actual also
        denotes a subtype.


                              Static Semantics

5   {generic formal type} {formal type} {generic formal subtype} {formal
subtype} A formal_type_declaration declares a (generic) formal type, and its
first subtype, the (generic) formal subtype.

        5.a   Ramification:  A subtype (other than the first subtype) of a
        generic formal type is not a generic formal subtype.

6   {determined class for a formal type} {class determined for a formal type}
The form of a formal_type_definition determines a class to which the formal
type belongs.  For a formal_private_type_definition the reserved words tagged
and limited indicate the class (see 12.5.1).  For a formal_derived_type_
definition the class is the derivation class rooted at the ancestor type.
For other formal types, the name of the syntactic category indicates the
class; a formal_discrete_type_definition defines a discrete type, and so on.

        6.a   Reason:  This rule is clearer with the flat syntax rule for
        formal_type_definition given above.  Adding formal_integer_type_
        definition and others would make this rule harder to state clearly.


                               Legality Rules

7   The actual type shall be in the class determined for the formal.

        7.a   Ramification:  For example, if the class determined for the
        formal is the class of all discrete types, then the actual has to be
        discrete.

        7.b   Note that this rule does not require the actual to belong to
        every class to which the formal belongs.  For example, formal private
        types are in the class of composite types, but the actual need not be
        composite.  Furthermore, one can imagine an infinite number of
        classes that are just arbitrary sets of types that obey the
        closed-under-derivation rule, and are therefore technically classes
        (even though we don't give them names, since they are uninteresting).
        We don't want this rule to apply to those classes.

        7.c   ``Limited'' is not a ``interesting'' class, but ``nonlimited''
        is; it is legal to pass a nonlimited type to a limited formal type,
        but not the other way around.  The reserved word limited really
        represents a class containing both limited and nonlimited types.
        ``Private'' is not a class; a generic formal private type accepts
        both private and nonprivate actual types.

        7.d   It is legal to pass a class-wide subtype as the actual if it is
        in the right class, so long as the formal has unknown discriminants.


                              Static Semantics

8   [The formal type also belongs to each class that contains the determined
class.]  The primitive subprograms of the type are as for any type in the
determined class.  For a formal type other than a formal derived type, these
are the predefined operators of the type; they are implicitly declared
immediately after the declaration of the formal type.  In an instance, the
copy of such an implicit declaration declares a view of the predefined
operator of the actual type, even if this operator has been overridden for
the actual type.  [The rules specific to formal derived types are given in
12.5.1.]

        8.a   Ramification:  All properties of the type are as for any type
        in the class.  Some examples:  The primitive operations available are
        as defined by the language for each class.  The form of constraint
        applicable to a formal type in a subtype_indication depends on the
        class of the type as for a nonformal type.  The formal type is tagged
        if and only if it is declared as a tagged private type, or as a type
        derived from a (visibly) tagged type.  (Note that the actual type
        might be tagged even if the formal type is not.)


     NOTES
9    (7) Generic formal types, like all types, are not named.  Instead, a
     name can denote a generic formal subtype.  Within a generic unit, a
     generic formal type is considered as being distinct from all other
     (formal or nonformal) types.

   9.a   Proof:  This follows from the fact that each formal_type_declaration
        declares a type.

10   (8) A discriminant_part is allowed only for certain kinds of types, and
     therefore only for certain kinds of generic formal types.  See 3.7.

   10.a   Ramification:  The term ``formal floating point type'' refers to a
        type defined by a formal_floating_point_definition.  It does not
        include a formal derived type whose ancestor is floating point.
        Similar terminology applies to the other kinds of formal_type_
        definition.


                                  Examples

11   Examples of generic formal types:

12  type Item is private;
    type Buffer(Length : Natural) is limited private;

13  type Enum  is (<>);
    type Int   is range <>;
    type Angle is delta <>;
    type Mass  is digits <>;

14  type Table is array (Enum) of Item;

15   Example of a generic formal part declaring a formal integer type:

16  generic
       type Rank is range <>;
       First  : Rank := Rank'First;
       Second : Rank := First + 1;  --  the operator "+" of the type Rank


                         Wording Changes From Ada 83

        16.a   RM83 has separate sections ``Generic Formal Xs'' and
        ``Matching Rules for Formal Xs'' (for various X's) with most of the
        text redundant between the two.  We have combined the two in order to
        reduce the redundancy.  In RM83, there is no ``Matching Rules for
        Formal Types'' section; nor is there a ``Generic Formal Y Types''
        section (for Y = Private, Scalar, Array, and Access).  This causes,
        for example, the duplication across all the ``Matching Rules for Y
        Types'' sections of the rule that the actual passed to a formal type
        shall be a subtype; the new organization avoids that problem.

        16.b   The matching rules are stated more concisely.

        16.c   We no longer consider the multiplying operators that deliver a
        result of type universal_fixed to be predefined for the various
        types; there is only one of each in package Standard.  Therefore, we
        need not mention them here as RM83 had to.



12.5.1 Formal Private and Derived Types

1   [The class determined for a formal private type can be either limited or
nonlimited, and either tagged or untagged; no more specific class is known
for such a type.  The class determined for a formal derived type is the
derivation class rooted at the ancestor type.]


                                   Syntax

2   formal_private_type_definition ::= [[abstract] tagged] [limited] private

3   formal_derived_type_definition ::= [abstract] new subtype_mark [with privat\
e]


                               Legality Rules

4   If a generic formal type declaration has a known_discriminant_part, then
it shall not include a default_expression for a discriminant.

        4.a   Ramification:  Consequently, a generic formal subtype with a
        known_discriminant_part is an indefinite subtype, so the declaration
        of a stand-alone variable has to provide a constraint on such a
        subtype, either explicitly, or by its initial value.

5   {ancestor subtype (of a formal derived type)} The ancestor subtype of a
formal derived type is the subtype denoted by the subtype_mark of the formal_
derived_type_definition.  For a formal derived type declaration, the reserved
words with private shall appear if and only if the ancestor type is a tagged
type; in this case the formal derived type is a private extension of the
ancestor type and the ancestor shall not be a class-wide type.  [Similarly,
the optional reserved word abstract shall appear only if the ancestor type is
a tagged type].

        5.a   Reason:  We use the term ``ancestor'' here instead of
        ``parent'' because the actual can be any descendant of the ancestor,
        not necessarily a direct descendant.

6   If the formal subtype is definite, then the actual subtype shall also be
definite.

        6.a   Ramification:  On the other hand, for an indefinite formal
        subtype, the actual can be either definite or indefinite.

7   For a generic formal derived type with no discriminant_part:

    8  If the ancestor subtype is constrained, the actual subtype shall
       be constrained, and shall be statically compatible with the
       ancestor;

 8.a    Ramification:  In other words, any constraint on the ancestor
        subtype is considered part of the ``contract.''

    9  If the ancestor subtype is an unconstrained access or composite
       subtype, the actual subtype shall be unconstrained.

 9.a    Reason:  This rule ensures that if a composite constraint is
        allowed on the formal, one is also allowed on the actual.  If
        the ancestor subtype is an unconstrained scalar subtype, the
        actual is allowed to be constrained, since a scalar constraint
        does not cause further constraints to be illegal.

   10  If the ancestor subtype is an unconstrained discriminated
       subtype, then the actual shall have the same number of
       discriminants, and each discriminant of the actual shall
       correspond to a discriminant of the ancestor, in the sense of
       3.7.  {94-4777.a}

 10.a   Reason:  This ensures that if a discriminant constraint is given
        on the formal subtype, the corresponding constraint in the
        instance will make sense, without additional run-time checks.
        This is not necessary for arrays, since the bounds cannot be
        overridden in a type extension.  An unknown_discriminant_part
        may be used to relax these matching requirements.

11   The declaration of a formal derived type shall not have a known_
discriminant_part.  For a generic formal private type with a known_
discriminant_part:  {94-4777.a}

   12  The actual type shall be a type with the same number of
       discriminants.

   13  The actual subtype shall be unconstrained.

   14  The subtype of each discriminant of the actual type shall
       statically match the subtype of the corresponding discriminant of
       the formal type.  {statically matching [required]}

 14.a   Reason:  We considered defining the first and third rule to be
        called ``subtype conformance'' for discriminant_parts.  We
        rejected that idea, because it would require implicit
        (inherited) discriminant_parts, which seemed like too much
        mechanism.

15   [For a generic formal type with an unknown_discriminant_part, the actual
may, but need not, have discriminants, and may be definite or indefinite.]
{94-4474.a}


                              Static Semantics

16   The class determined for a formal private type is as follows:

17  Type Definition                               Determined Class

    limited private                                             the class of al\
l types
    private                                                     the class of al\
l nonlimited types
    tagged limited private                                      the class of al\
l tagged types
    tagged private                                              the class of al\
l nonlimited tagged types

18   [The presence of the reserved word abstract determines whether the
actual type may be abstract.]

19   A formal private or derived type is a private or derived type,
respectively.  A formal derived tagged type is a private extension.  [A
formal private or derived type is abstract if the reserved word abstract
appears in its declaration.]

20   If the ancestor type is a composite type that is not an array type, the
formal type inherits components from the ancestor type (including
discriminants if a new discriminant_part is not specified), as for a derived
type defined by a derived_type_definition (see 3.4).

21   For a formal derived type, the predefined operators and inherited
user-defined subprograms are determined by the ancestor type, and are
implicitly declared at the earliest place, if any, within the immediate scope
of the formal type, where the corresponding primitive subprogram of the
ancestor is visible (see 7.3.1).  In an instance, the copy of such an
implicit declaration declares a view of the corresponding primitive
subprogram of the ancestor, even if this primitive has been overridden for
the actual type.  [In the case of a formal private extension, however, the
tag of the formal type is that of the actual type, so if the tag in a call is
statically determined to be that of the formal type, the body executed will
be that corresponding to the actual type.]

        21.a   Ramification:  The above rule defining the properties of
        primitive subprograms in an instance applies even if the subprogram
        has been overridden or hidden for the actual type.  This rule is
        necessary for untagged types, because their primitive subprograms
        might have been overridden by operations that are not
        subtype-conformant with the operations defined for the class.  For
        tagged types, the rule still applies, but the primitive subprograms
        will dispatch to the appropriate implementation based on the type and
        tag of the operands.  Even for tagged types, the formal parameter
        names and default_expressions are determined by those of the
        primitive subprograms of the specified ancestor type.

22   For a prefix S that denotes a formal indefinite subtype, the following
attribute is defined:

23  S'Definite
                S'Definite yields True if the actual subtype corresponding to
                S is definite; otherwise it yields False.  The value of this
                attribute is of the predefined type Boolean.

23.a    Discussion:  Whether an actual subtype is definite or indefinite may
        have a major effect on the algorithm used in a generic.  For example,
        in a generic I/O package, whether to use fixed-length or
        variable-length records could depend on whether the actual is
        definite or indefinite.  This attribute is essentially a replacement
        for the Constrained attribute which is now considered obsolete.


     NOTES
24   (9) In accordance with the general rule that the actual type shall
     belong to the class determined for the formal (see 12.5, ``Formal
     Types''):

        25  If the formal type is nonlimited, then so shall be the
            actual;

        26  For a formal derived type, the actual shall be in the class
            rooted at the ancestor subtype.

27   (10) [The actual type can be abstract only if the formal type is
     abstract (see 3.9.3).]

   27.a   Reason:  This is necessary to avoid contract model problems, since
        one or more of its primitive subprograms are abstract; it is
        forbidden to create objects of the type, or to declare functions
        returning the type.

   27.b   Ramification:  On the other hand, it is OK to pass a non-abstract
        actual to an abstract formal -- abstract on the formal indicates that
        the actual might be abstract.

28   (11) If the formal has a discriminant_part, the actual can be either
     definite or indefinite.  Otherwise, the actual has to be definite.


                        Incompatibilities With Ada 83

        28.a   {incompatibilities with Ada 83} Ada 83 does not have unknown_
        discriminant_parts, so it allows indefinite subtypes to be passed to
        definite formals, and applies a legality rule to the instance body.
        This is a contract model violation.  Ada 9X disallows such cases at
        the point of the instantiation.  The workaround is to add (<>) as the
        discriminant_part of any formal subtype if it is intended to be used
        with indefinite actuals.  If that's the intent, then there can't be
        anything in the generic body that would require a definite subtype.

        28.b   The check for discriminant subtype matching is changed from a
        run-time check to a compile-time check.



12.5.2 Formal Scalar Types

1   A formal scalar type is one defined by any of the formal_type_definitions
in this subclause.  [The class determined for a formal scalar type is
discrete, signed integer, modular, floating point, ordinary fixed point, or
decimal.]


                                   Syntax

2   formal_discrete_type_definition ::= (<>)

3   formal_signed_integer_type_definition ::= range <>

4   formal_modular_type_definition ::= mod <>

5   formal_floating_point_definition ::= digits <>

6   formal_ordinary_fixed_point_definition ::= delta <>

7   formal_decimal_fixed_point_definition ::= delta <> digits <>


                               Legality Rules

8   The actual type for a formal scalar type shall not be a nonstandard
numeric type.

        8.a   Reason:  This restriction is necessary because nonstandard
        numeric types have some number of restrictions on their use, which
        could cause contract model problems in a generic body.  Note that
        nonstandard numeric types can be passed to formal derived and formal
        private subtypes, assuming they obey all the other rules, and
        assuming the implementation allows it (being nonstandard means the
        implementation might disallow anything).


     NOTES
9    (12) The actual type shall be in the class of types implied by the
     syntactic category of the formal type definition (see 12.5, ``Formal
     Types'').  For example, the actual for a formal_modular_type_definition
     shall be a modular type.



12.5.3 Formal Array Types

1   [The class determined for a formal array type is the class of all array
types.]


                                   Syntax

2   formal_array_type_definition ::= array_type_definition


                               Legality Rules

3   The only form of discrete_subtype_definition that is allowed within the
declaration of a generic formal (constrained) array subtype is a subtype_
mark.

        3.a   Reason:  The reason is the same as for forbidding constraints
        in subtype_indications (see 12.1).

4   For a formal array subtype, the actual subtype shall satisfy the
following conditions:

    5  The formal array type and the actual array type shall have the
       same dimensionality; the formal subtype and the actual subtype
       shall be either both constrained or both unconstrained.

    6  For each index position, the index types shall be the same, and
       the index subtypes (if unconstrained), or the index ranges (if
       constrained), shall statically match (see 4.9.1).  {statically
       matching [required]}

    7  The component subtypes of the formal and actual array types shall
       statically match.  {statically matching [required]}

    8  If the formal type has aliased components, then so shall the
       actual.

 8.a    Ramification:  On the other hand, if the formal's components are
        not aliased, then the actual's components can be either aliased
        or not.


                                  Examples

9   Example of formal array types:

10  --  given the generic package

11  generic
       type Item   is private;
       type Index  is (<>);
       type Vector is array (Index range <>) of Item;
       type Table  is array (Index) of Item;
    package P is
       ...
    end P;
12  --  and the types

13  type Mix    is array (Color range <>) of Boolean;
    type Option is array (Color) of Boolean;

14  --  then Mix can match Vector and Option can match Table

15  package R is new P(Item   => Boolean, Index => Color,
                       Vector => Mix,     Table => Option);

16  --  Note that Mix cannot match Table and Option cannot match Vector


                        Incompatibilities With Ada 83

        16.a   {incompatibilities with Ada 83} The check for matching of
        component subtypes and index subtypes or index ranges is changed from
        a run-time check to a compile-time check.  The Ada 83 rule that ``If
        the component type is not a scalar type, then the component subtypes
        shall be either both constrained or both unconstrained'' is removed,
        since it is subsumed by static matching.  Likewise, the rules
        requiring that component types be the same is subsumed.



12.5.4 Formal Access Types

1   [The class determined for a formal access type is the class of all access
types.]


                                   Syntax

2   formal_access_type_definition ::= access_type_definition


                               Legality Rules

3   For a formal access-to-object type, the designated subtypes of the formal
and actual types shall statically match.  {statically matching [required]}

4   If and only if the general_access_modifier constant applies to the
formal, the actual shall be an access-to-constant type.  If the general_
access_modifier all applies to the formal, then the actual shall be a general
access-to-variable type (see 3.10).

        4.a   Ramification:  If no _modifier applies to the formal, then the
        actual type may be either a pool-specific or a general
        access-to-variable type.

5   For a formal access-to-subprogram subtype, the designated profiles of the
formal and the actual shall be mode-conformant, and the calling convention of
the actual shall be protected if and only if that of the formal is protected.
{mode conformance (required)}

        5.a   Reason:  We considered requiring subtype conformance here, but
        mode conformance is more flexible, given that there is no way in
        general to specify the convention of the formal.


                                  Examples

6   Example of formal access types:

7   --  the formal types of the generic package

8   generic
       type Node is private;
       type Link is access Node;
    package P is
       ...
    end P;

9   --  can be matched by the actual types

10  type Car;
    type Car_Name is access Car;

11  type Car is
       record
          Pred, Succ : Car_Name;
          Number     : License_Number;
          Owner      : Person;
       end record;

12  --  in the following generic instantiation

13  package R is new P(Node => Car, Link => Car_Name);


                        Incompatibilities With Ada 83

        13.a   {incompatibilities with Ada 83} The check for matching of
        designated subtypes is changed from a run-time check to a
        compile-time check.  The Ada 83 rule that ``If the designated type is
        other than a scalar type, then the designated subtypes shall be
        either both constrained or both unconstrained'' is removed, since it
        is subsumed by static matching.

                            Extensions to Ada 83

        13.b   {extensions to Ada 83} Formal access-to-subprogram subtypes
        and formal general access types are new concepts.



12.6 Formal Subprograms

1   [{generic formal subprogram} {formal subprogram, generic} Formal
subprograms can be used to pass callable entities to a generic unit.]


                         Language Design Principles

        1.a   Generic formal subprograms are like renames of the explicit_
        generic_actual_parameter.

                                   Syntax

2   formal_subprogram_declaration ::= with subprogram_specification [is subprog\
ram_default];

3   subprogram_default ::= default_name | <>

4   default_name ::= name


                            Name Resolution Rules

5   {expected profile [formal subprogram default_name]} The expected profile
for the default_name, if any, is that of the formal subprogram.

        5.a   Ramification:  This rule, unlike others in this clause, is
        observed at compile time of the generic_declaration.

        5.b   The evaluation of the default_name takes place during the
        elaboration of each instantiation that uses the default, as defined
        in 12.3, ``Generic Instantiation''.

6   {expected profile [formal subprogram actual]} For a generic formal
subprogram, the expected profile for the actual is that of the formal
subprogram.


                               Legality Rules

7   The profiles of the formal and any named default shall be
mode-conformant.  {mode conformance (required)}

        7.a   Ramification:  This rule, unlike others in this clause, is
        checked at compile time of the generic_declaration.

8   The profiles of the formal and actual shall be mode-conformant.  {mode
conformance (required)}


                              Static Semantics

9   A formal_subprogram_declaration declares a generic formal subprogram.
The types of the formal parameters and result, if any, of the formal
subprogram are those determined by the subtype_marks given in the formal_
subprogram_declaration; however, independent of the particular subtypes that
are denoted by the subtype_marks, the nominal subtypes of the formal
parameters and result, if any, are defined to be nonstatic, and unconstrained
if of an array type [(no applicable index constraint is provided in a call on
a formal subprogram)].  In an instance, a formal_subprogram_declaration
declares a view of the actual.  The profile of this view takes its subtypes
and calling convention from the original profile of the actual entity, while
taking the formal parameter names and default_expressions from the profile
given in the formal_subprogram_declaration.  The view is a function or
procedure, never an entry.

        9.a   Discussion:  This rule is intended to be the same as the one
        for renamings-as-declarations, where the formal_subprogram_decla-
        ration is analogous to a renaming-as-declaration, and the actual is
        analogous to the renamed view.

10   If a generic unit has a subprogram_default specified by a box, and the
corresponding actual parameter is omitted, then it is equivalent to an
explicit actual parameter that is a usage name identical to the defining name
of the formal.


     NOTES
11   (13) The matching rules for formal subprograms state requirements that
     are similar to those applying to subprogram_renaming_declarations (see
     8.5.4).  In particular, the name of a parameter of the formal subprogram
     need not be the same as that of the corresponding parameter of the
     actual subprogram; similarly, for these parameters, default_expressions
     need not correspond.

12   (14) The constraints that apply to a parameter of a formal subprogram
     are those of the corresponding formal parameter of the matching actual
     subprogram (not those implied by the corresponding subtype_mark in the
     _specification of the formal subprogram).  A similar remark applies to
     the result of a function.  Therefore, to avoid confusion, it is
     recommended that the name of a first subtype be used in any declaration
     of a formal subprogram.

13   (15) The subtype specified for a formal parameter of a generic formal
     subprogram can be any visible subtype, including a generic formal
     subtype of the same generic_formal_part.

14   (16) A formal subprogram is matched by an attribute of a type if the
     attribute is a function with a matching specification.  An enumeration
     literal of a given type matches a parameterless formal function whose
     result type is the given type.

15   (17) A default_name denotes an entity that is visible or directly
     visible at the place of the generic_declaration; a box used as a default
     is equivalent to a name that denotes an entity that is directly visible
     at the place of the _instantiation.

   15.a   Proof:  Visibility and name resolution are applied to the
        equivalent explicit actual parameter.

16   (18) The actual subprogram cannot be abstract (see 3.9.3).


                                  Examples

17   Examples of generic formal subprograms:

18  with function "+"(X, Y : Item) return Item is <>;
    with function Image(X : Enum) return String is Enum'Image;
    with procedure Update is Default_Update;

19  --  given the generic procedure declaration

20  generic
       with procedure Action (X : in Item);
    procedure Iterate(Seq : in Item_Sequence);

21  --  and the procedure

22  procedure Put_Item(X : in Item);

23  --  the following instantiation is possible

24  procedure Put_List is new Iterate(Action => Put_Item);



12.7 Formal Packages

1   [{generic formal package} {formal package, generic} Formal packages can
be used to pass packages to a generic unit.  The formal_package_declaration
declares that the formal package is an instance of a given generic package.
Upon instantiation, the actual package has to be an instance of that generic
package.]


                                   Syntax

2   formal_package_declaration ::=
        with package defining_identifier is new generic_package_name  formal_pa\
ckage_actual_part;

3   formal_package_actual_part ::=
        (<>) | [generic_actual_part]


                               Legality Rules

4   {template (for a formal package)} The generic_package_name shall denote a
generic package (the template for the formal package); the formal package is
an instance of the template.

5   The actual shall be an instance of the template.  If the formal_package_
actual_part is (<>), [then the actual may be any instance of the template];
otherwise, each actual parameter of the actual instance shall match the
corresponding actual parameter of the formal package [(whether the actual
parameter is given explicitly or by default)], as follows:

    6  For a formal object of mode in the actuals match if they are
       static expressions with the same value, or if they statically
       denote the same constant, or if they are both the literal null.

 6.a    Reason:  We can't simply require full conformance between the
        two actual parameter expressions, because the two expressions
        are being evaluated at different times.

    7  For a formal subtype, the actuals match if they denote statically
       matching subtypes.  {statically matching [required]}

    8  For other kinds of formals, the actuals match if they statically
       denote the same entity.


                              Static Semantics

9   A formal_package_declaration declares a generic formal package.

10   {visible part [of a formal package]} The visible part of a formal
package includes the first list of basic_declarative_items of the package_
specification.  In addition, if the formal_package_actual_part is (<>), it
also includes the generic_formal_part of the template for the formal package.

        10.a   Ramification:  If the formal_package_actual_part is (<>), then
        the declarations that occur immediately within the generic_formal_
        part of the template for the formal package are visible outside the
        formal package, and can be denoted by expanded names outside the
        formal package.

        10.b   Reason:  We always want either the actuals or the formals of
        an instance to be namable from outside, but never both.  If both were
        namable, one would get some funny anomalies since they denote the
        same entity, but, in the case of types at least, they might have
        different and inconsistent sets of primitive operators due to
        predefined operator ``reemergence.''  Formal derived types exacerbate
        the difference.  We want the implicit declarations of the generic_
        formal_part as well as the explicit declarations, so we get
        operations on the formal types.

        10.c   Ramification:  A generic formal package is a package, and is
        an instance.  Hence, it is possible to pass a generic formal package
        as an actual to another generic formal package.


                            Extensions to Ada 83

        10.d   {extensions to Ada 83} Formal packages are new to Ada 9X.



12.8 Example of a Generic Package

1   The following example provides a possible formulation of stacks by means
of a generic package.  The size of each stack and the type of the stack
elements are provided as generic formal parameters.


                                  Examples

2

3   generic
       Size : Positive;
       type Item is private;
    package Stack is
       procedure Push(E : in  Item);
       procedure Pop (E : out Item);
       Overflow, Underflow : exception;
    end Stack;

4   package body Stack is

5      type Table is array (Positive range <>) of Item;
       Space : Table(1 .. Size);
       Index : Natural := 0;

6      procedure Push(E : in Item) is
       begin
          if Index >= Size then
             raise Overflow;
          end if;
          Index := Index + 1;
          Space(Index) := E;
       end Push;

7      procedure Pop(E : out Item) is
       begin
          if Index = 0 then
             raise Underflow;
          end if;
          E := Space(Index);
          Index := Index - 1;
       end Pop;

8   end Stack;

9   Instances of this generic package can be obtained as follows:

10  package Stack_Int  is new Stack(Size => 200, Item => Integer);
    package Stack_Bool is new Stack(100, Boolean);

11   Thereafter, the procedures of the instantiated packages can be called as
follows:

12  Stack_Int.Push(N);
    Stack_Bool.Push(True);

13   Alternatively, a generic formulation of the type Stack can be given as
follows (package body omitted):

14  generic
       type Item is private;
    package On_Stacks is
       type Stack(Size : Positive) is limited private;
       procedure Push(S : in out Stack; E : in  Item);
       procedure Pop (S : in out Stack; E : out Item);
       Overflow, Underflow : exception;
    private
       type Table is array (Positive range <>) of Item;
       type Stack(Size : Positive) is
          record
             Space : Table(1 .. Size);
             Index : Natural := 0;
          end record;
    end On_Stacks;

15   In order to use such a package, an instance has to be created and
thereafter stacks of the corresponding type can be declared:

16  declare
       package Stack_Real is new On_Stacks(Real); use Stack_Real;
       S : Stack(100);
    begin
       ...
       Push(S, 2.54);
       ...
    end;



                      Section 13: Representation Issues


1   [This section describes features for querying and controlling aspects of
representation and for interfacing to hardware.

        1.a   Change:  Changed the name of Section 13, and reworded the
        introductory paragraph, as per WG9 resolution.

]


                         Wording Changes From Ada 83

        1.b   The clauses of this section have been reorganized.  This was
        necessary to preserve a logical order, given the new Ada 9X semantics
        given in this section.



13.1 Representation Items

1   {representation item} {representation pragma [distributed]} {pragma,
representation [distributed]} There are three kinds of representation items:
representation_clauses, component_clauses, and representation pragmas.
[Representation items specify how the types and other entities of the
language are to be mapped onto the underlying machine.  They can be provided
to give more efficient representation or to interface with features that are
outside the domain of the language (for example, peripheral hardware).
Representation items also specify other specifiable properties of entities.
A representation item applies to an entity identified by a local_name, which
denotes an entity declared local to the current declarative region, or a
library unit declared immediately preceding a representation pragma in a
compilation.]


                                   Syntax

2   representation_clause ::= attribute_definition_clause
          | enumeration_representation_clause
          | record_representation_clause
          | at_clause

3   local_name ::= direct_name
          | direct_name'attribute_designator
          | library_unit_name

    4   A representation pragma is allowed only at places where a
    representation_clause or compilation_unit is allowed.


                            Name Resolution Rules

5   In a representation item, if the local_name is a direct_name, then it
shall resolve to denote a declaration (or, in the case of a pragma, one or
more declarations) that occurs immediately within the same declarative_region
as the representation item.  If the local_name has an attribute_designator,
then it shall resolve to denote an implementation-defined component (see
13.5.1) or a class-wide type implicitly declared immediately within the same
declarative_region as the representation item.  A local_name that is a
library_unit_name (only permitted in a representation pragma) shall resolve
to denote the library_item that immediately precedes (except for other
pragmas) the representation pragma.

        5.a   Reason:  This is a Name Resolution Rule, because we don't want
        a representation item for X to be ambiguous just because there's
        another X declared in an outer declarative region.  It doesn't make
        much difference, since most representation items are for types or
        subtypes, and type and subtype names can't be overloaded.

        5.b   Ramification:  The visibility rules imply that the declaration
        has to occur before the representation item.

        5.c   For objects, this implies that representation items can be
        applied only to stand-alone objects.


                               Legality Rules

6   The local_name of a representation_clause or representation pragma shall
statically denote an entity (or, in the case of a pragma, one or more
entities) declared immediately preceding it in a compilation, or within the
same declarative_part, package_specification, task_definition, protected_
definition, or record_definition as the representation item.  If a local_name
denotes a [local] callable entity, it may do so through a [local] subprogram_
renaming_declaration [(as a way to resolve ambiguity in the presence of
overloading)]; otherwise, the local_name shall not denote a renaming_
declaration.

        6.a   Ramification:  The ``statically denote'' part implies that it
        is impossible to specify the representation of an object that is not
        a stand-alone object, except in the case of a representation item
        like pragma Atomic that is allowed inside a component_list (in which
        case the representation item specifies the representation of
        components of all objects of the type).  It also prevents the problem
        of renamings of things like ``P.all'' (where P is an
        access-to-subprogram value) or ``E(I)'' (where E is an entry family).

        6.b   The part about where the denoted entity has to have been
        declared appears twice -- once as a Name Resolution Rule, and once as
        a Legality Rule.  Suppose P renames Q, and we have a representation
        item in a declarative_part whose local_name is P. The fact that the
        representation item has to appear in the same declarative_part as P
        is a Name Resolution Rule, whereas the fact that the representation
        item has to appear in the same declarative_part as Q is a Legality
        Rule.  This is subtle, but it seems like the least confusing set of
        rules.

        6.c   Discussion:  A separate Legality Rule applies for component_
        clauses.  See 13.5.1, ``Record Representation Clauses''.

7   {representation of an object} {size (of an object)} The representation of
an object consists of a certain number of bits (the size of the object).
These are the bits that are normally read or updated by the machine code when
loading, storing, or operating-on the value of the object.  This includes
some padding bits, when the size of the object is greater than the size of
its subtype.  {gaps} {padding bits} Such padding bits are considered to be
part of the representation of the object, rather than being gaps between
objects, if these bits are normally read and updated.

        7.a   To be honest:  {contiguous representation [partial]}
        {discontiguous representation [partial]} Discontiguous represen-
        tations are allowed, but the ones we're interested in here are
        generally contiguous sequences of bits.

        7.b   Ramification:  Two objects with the same value do not
        necessarily have the same representation.  For example, an
        implementation might represent False as zero and True as any odd
        value.  Similarly, two objects (of the same type) with the same
        sequence of bits do not necessarily have the same value.  For
        example, an implementation might use a biased representation in some
        cases but not others:

7.c         subtype S is Integer range 1..256;
            type A is array(Natural range 1..4) of S;
            pragma Pack(A);
            X : S := 3;
            Y : A := (1, 2, 3, 4);

        7.d   The implementation might use a biased-by-1 representation for
        the array elements, but not for X. X and Y(3) have the same value,
        but different representation:  the representation of X is a sequence
        of (say) 32 bits: 0...011, whereas the representation of Y(3) is a
        sequence of 8 bits:  00000010 (assuming a two's complement
        representation).

        7.e   Such tricks are not required, but are allowed.

        7.f   Discussion:  The value of any padding bits is not specified by
        the language, though for a numeric type, it will be much harder to
        properly implement the predefined operations if the padding bits are
        not either all zero, or a sign extension.

        7.g   Ramification:  For example, suppose S'Size = 2, and an object X
        is of subtype S. If the machine code typically uses a 32-bit load
        instruction to load the value of X, then X'Size should be 32, even
        though 30 bits of the value are just zeros or sign-extension bits.
        {94-4539.c} On the other hand, if the machine code typically masks
        out those 30 bits, then X'Size should be 2.  Usually, such masking
        only happens for components of a composite type for which packing,
        Component_Size, or record layout is specified.

        7.h   Note, however, that the formal parameter of an instance of
        Unchecked_Conversion is a special case.  Its Size is required to be
        the same as that of its subtype.

        7.i   Note that we don't generally talk about the representation of a
        value.  A value is considered to be an amorphous blob without any
        particular representation.  An object is considered to be more
        concrete.

8   {aspect of representation [distributed]} {representation aspect}
{directly specified (of an aspect of representation of an entity)} A
representation item directly specifies an aspect of representation of the
entity denoted by the local_name, except in the case of a type-related
representation item, whose local_name shall denote a first subtype, and which
directly specifies an aspect of the subtype's type.  {type-related
(representation item) [distributed]} {subtype-specific (of a representation
item) [distributed]} {type-related (aspect) [distributed]} {subtype-specific
(of an aspect) [distributed]} A representation item that names a subtype is
either subtype-specific (Size and Alignment clauses) or type-related (all
others).  [Subtype-specific aspects may differ for different subtypes of the
same type.]
        8.a   To be honest:  Type-related and subtype-specific are defined
        likewise for the corresponding aspects of representation.

        8.b   To be honest:  Some representation items directly specify more
        than one aspect.

        8.c   Discussion:  For example, a pragma Export specifies the
        convention of an entity, and also specifies that it is exported.

        8.d   Ramification:  Each specifiable attribute constitutes a
        separate aspect.  An enumeration_representation_clause specifies the
        coding aspect.  A record_representation_clause (without the mod_
        clause) specifies the record layout aspect.  Each representation
        pragma specifies a separate aspect.

        8.e   Reason:  We don't need to say that an at_clause or a mod_clause
        specify separate aspects, because these are equivalent to attribute_
        definition_clauses.  See J.7, ``At Clauses'', and J.8, ``Mod
        Clauses''.

        8.f   Ramification:  The following representation items are
        type-related:

          8.g  enumeration_representation_clause

          8.h  record_representation_clause

          8.i  Component_Size clause

          8.j  External_Tag clause

          8.k  Small clause

          8.l  Bit_Order clause

          8.m  Storage_Pool clause

          8.n  Storage_Size clause

          8.o  Read clause

          8.p  Write clause

          8.q  Input clause

          8.r  Output clause

          8.s  Machine_Radix clause

          8.t  pragma Pack

          8.u  pragmas Import, Export, and Convention (when applied to a
               type)

          8.v  pragmas Atomic and Volatile (when applied to a type)

          8.w  pragmas Atomic_Components and Volatile_Components (when
               applied to an array type)

          8.x  pragma Discard_Names (when applied to an enumeration or
               tagged type)

        8.y   The following representation items are subtype-specific:

          8.z  Alignment clause (when applied to a first subtype)

         8.aa  Size clause (when applied to a first subtype)

        8.bb   The following representation items do not apply to subtypes,
        so they are neither type-related nor subtype-specific:

         8.cc  Address clause (applies to objects and program units)

         8.dd  Alignment clause (when applied to an object)

         8.ee  Size clause (when applied to an object)

         8.ff  pragmas Import, Export, and Convention (when applied to
               anything other than a type)

         8.gg  pragmas Atomic and Volatile (when applied to an object or
               a component)

         8.hh  pragmas Atomic_Components and Volatile_Components (when
               applied to an array object)

         8.ii  pragma Discard_Names (when applied to an exception)

         8.jj  pragma Asynchronous (applies to procedures)

9   A representation item that directly specifies an aspect of a subtype or
type shall appear after the type is completely defined (see 3.11.1), and
before the subtype or type is frozen (see 13.14).  If a representation item
is given that directly specifies an aspect of an entity, then it is illegal
to give another representation item that directly specifies the same aspect
of the entity.

        9.a   Ramification:  The fact that a representation item that
        directly specifies an aspect of an entity is required to appear
        before the entity is frozen prevents changing the representation of
        an entity after using the entity in ways that require the
        representation to be known.

10   For an untagged derived type, no type-related representation items are
allowed if the parent type is a by-reference type, or has any user-defined
primitive subprograms.

        10.a   Ramification:  On the other hand, subtype-specific
        representation items may be given for the first subtype of such a
        type.

        10.b   Reason:  The reason for forbidding type-related representation
        items on untagged by-reference types is because a change of
        representation is impossible when passing by reference (to an
        inherited subprogram).  The reason for forbidding type-related
        representation items on untagged types with user-defined primitive
        subprograms was to prevent implicit change of representation for
        type-related aspects of representation upon calling inherited
        subprograms, because such changes of representation are likely to be
        expensive at run time.  Changes of subtype-specific representation
        attributes, however, are likely to be cheap.  This rule is not needed
        for tagged types, because other rules prevent a type-related
        representation item from changing the representation of the parent
        part; we want to allow a type-related representation item on a type
        extension to specify aspects of the extension part.  For example, a
        pragma Pack will cause packing of the extension part, but not of the
        parent part.

11   Representation aspects of a generic formal parameter are the same as
those of the actual.  A type-related representation item is not allowed for a
descendant of a generic formal untagged type.

        11.a   Ramification:  Representation items are allowed for types
        whose subcomponent types or index subtypes are generic formal types.

        11.b   Reason:  Since it is not known whether a formal type has
        user-defined primitive subprograms, specifying type-related represen-
        tation items for them is not allowed, unless they are tagged (in
        which case only the extension part is affected in any case).

12   A representation item that specifies the Size for a given subtype, or
the size or storage place for an object (including a component) of a given
subtype, shall allow for enough storage space to accommodate any value of the
subtype.

13   A representation item that is not supported by the implementation is
illegal, or raises an exception at run time.


                              Static Semantics

14   If two subtypes statically match, then their subtype-specific aspects
(Size and Alignment) are the same.  {statically matching [effect on
subtype-specific aspects]}

        14.a   Reason:  This is necessary because we allow (for example)
        conversion between access types whose designated subtypes statically
        match.  Note that it is illegal to specify an aspect (including a
        subtype-specific one) for a nonfirst subtype.

        14.b   Consider, for example:

14.c        package P1 is
                subtype S1 is Integer range 0..2**16-1;
                for S1'Size use 16; -- Illegal!
                    -- S1'Size would be 16 by default.
                type A1 is access S1;
                X1: A1;
            end P1;

14.d        package P2 is
                subtype S2 is Integer range 0..2**16-1;
                for S2'Size use 32; -- Illegal!
                type A2 is access S2;
                X2: A2;
            end P2;

14.e        procedure Q is
                use P1, P2;
                type Array1 is array(Integer range <>) of aliased S1;
                pragma Pack(Array1);
                Obj1: Array1(1..100);
                type Array2 is array(Integer range <>) of aliased S2;
                pragma Pack(Array2);
                Obj2: Array2(1..100);
            begin
                X1 := Obj2(17)'Access;
                X2 := Obj1(17)'Access;
            end Q;

        14.f   Loads and stores through X1 would read and write 16 bits, but
        X1 points to a 32-bit location.  Depending on the endianness of the
        machine, loads might load the wrong 16 bits.  Stores would fail to
        zero the other half in any case.

        14.g   Loads and stores through X2 would read and write 32 bits, but
        X2 points to a 16-bit location.  Thus, adjacent memory locations
        would be trashed.

        14.h   Hence, the above is illegal.  Furthermore, the compiler is
        forbidden from choosing different Sizes by default, for the same
        reason.

        14.i   The same issues apply to Alignment.  {94-5001.k}

15   A derived type inherits each type-related aspect of its parent type that
was directly specified before the declaration of the derived type, or (in the
case where the parent is derived) that was inherited by the parent type from
the grandparent type.  A derived subtype inherits each subtype-specific
aspect of its parent subtype that was directly specified before the
declaration of the derived type, or (in the case where the parent is derived)
that was inherited by the parent subtype from the grandparent subtype, but
only if the parent subtype statically matches the first subtype of the parent
type.  An inherited aspect of representation is overridden by a subsequent
representation item that specifies the same aspect of the type or subtype.

        15.a   To be honest:  A record_representation_clause for a record
        extension does not override the layout of the parent part; if the
        layout was specified for the parent type, it is inherited by the
        record extension.

        15.b   Ramification:  If a representation item for the parent appears
        after the derived_type_declaration, then inheritance does not happen
        for that representation item.

16   Each aspect of representation of an entity is as follows:

   17  {specified (of an aspect of representation of an entity)} If the
       aspect is specified for the entity, meaning that it is either
       directly specified or inherited, then that aspect of the entity
       is as specified, except in the case of Storage_Size, which
       specifies a minimum.

 17.a   Ramification:  This rule implies that queries of the aspect
        return the specified value.  For example, if the user writes
        ``for X'Size use 32;'', then a query of X'Size will return 32.

   18  {unspecified [partial]} If an aspect of representation of an
       entity is not specified, it is chosen by default in an
       unspecified manner.

        18.a   Ramification:  Note that representation_clauses can affect the
        semantics of the entity.

        18.b   The rules forbid things like ``for S'Base'Alignment use ...''
        and ``for S'Base use record ...''.

        18.c   Discussion:  The intent is that implementations will represent
        the components of a composite value in the same way for all subtypes
        of a given composite type.  Hence, Component_Size and record layout
        are type-related aspects.


                              Dynamic Semantics

19   {elaboration [representation_clause]} For the elaboration of a
representation_clause, any evaluable constructs within it are evaluated.

        19.a   Ramification:  Elaboration of representation pragmas is
        covered by the general rules for pragmas in Section 2.


                         Implementation Permissions

20   An implementation may interpret aspects of representation in an
implementation-defined manner.  An implementation may place implementation-
defined restrictions on representation items.  {recommended level of support
[distributed]} A recommended level of support is specified for representation
items and related features in each subclause.  These recommendations are
changed to requirements for implementations that support the Systems
Programming Annex (see C.2, ``Required Representation Support'').

        20.a   Implementation defined:  The interpretation of each aspect of
        representation.

        20.b   Implementation defined:  Any restrictions placed upon
        representation items.

        20.c   Ramification:  Implementation-defined restrictions may be
        enforced either at compile time or at run time.  There is no
        requirement that an implementation justify any such restrictions.
        They can be based on avoiding implementation complexity, or on
        avoiding excessive inefficiency, for example.


                            Implementation Advice

21   {recommended level of support [with respect to nonstatic expressions]}
The recommended level of support for all representation items is qualified as
follows:

   22  An implementation need not support representation items
       containing nonstatic expressions, except that an implementation
       should support a representation item for a given entity if each
       nonstatic expression in the representation item is a name that
       statically denotes a constant declared before the entity.

 22.a   Reason:  This is to avoid the following sort of thing:

22.b        X : Integer := F(...);
            Y : Address := G(...);
            for X'Address use Y;

 22.c   In the above, we have to evaluate the initialization expression
        for X before we know where to put the result.  This seems like
        an unreasonable implementation burden.

 22.d   The above code should instead be written like this:

22.e        Y : constant Address := G(...);
            X : Integer := F(...);
            for X'Address use Y;

 22.f   This allows the expression ``Y'' to be safely evaluated before X
        is created.

 22.g   The constant could be a formal parameter of mode in.

 22.h   An implementation can support other nonstatic expressions if it
        wants to.  Expressions of type Address are hardly ever static,
        but their value might be known at compile time anyway in many
        cases.

   23  An implementation need not support a specification for the Size
       for a given composite subtype, nor the size or storage place for
       an object (including a component) of a given composite subtype,
       unless the constraints on the subtype and its composite
       subcomponents (if any) are all static constraints.

   24  An aliased component, or a component whose type is by-reference,
       should always be allocated at an addressable location.

 24.a   Reason:  The intent is that access types, type System.Address,
        and the pointer used for a by-reference parameter should be
        implementable as a single machine address -- bit-field pointers
        should not be required.  (There is no requirement that this
        implementation be used -- we just want to make sure its
        feasible.)

 24.b   Implementation Note:  Note that the above rule does not apply to
        types that merely allow by-reference parameter passing; for such
        types, a copy typically needs to be made at the call site when a
        bit-aligned component is passed as a parameter.

 24.c   Ramification:  A pragma Pack will typically not pack so tightly
        as to disobey the above rule.  A Component_Size clause or
        record_representation_clause will typically by illegal if it
        disobeys the above rule.  Atomic components have similar
        restrictions (see C.6, ``Shared Variable Control'').


                        Incompatibilities With Ada 83

        24.d   {incompatibilities with Ada 83} It is now illegal for a
        representation item to cause a derived by-reference type to have a
        different record layout from its parent.  This is necessary for
        by-reference parameter passing to be feasible.  This only affects
        programs that specify the representation of types derived from types
        containing tasks; most by-reference types are new to Ada 9X.  For
        example, if A1 is an array of tasks, and A2 is derived from A1, it is
        illegal to apply a pragma Pack to A2.

                            Extensions to Ada 83

        24.e   {extensions to Ada 83} Ada 9X allows additional
        representation_clauses for objects.

                         Wording Changes From Ada 83

        24.f   The syntax rule for type_representation_clause is removed; the
        right-hand side of that rule is moved up to where it was used, in
        representation_clause.  There are two references to ``type
        representation clause'' in RM83, both in Section 13; these have been
        reworded.

        24.g   We have defined a new term ``representation item,'' which
        includes both representation_clauses and representation pragmas, as
        well as component_clauses.  This is convenient because the rules are
        almost identical for all three.

        24.h   All of the forcing occurrence stuff has been moved into its
        own subclause (see 13.14), and rewritten to use the term
        ``freezing''.

        24.i   RM83-13.1(10) requires implementation-defined restrictions on
        representation items to be enforced at compile time.  However, that
        is impossible in some cases.  If the user specifies a junk
        (nonstatic) address in an address clause, and the implementation
        chooses to detect the error (for example, using hardware memory
        management with protected pages), then it's clearly going to be a
        run-time error.  It seems silly to call that ``semantics'' rather
        than ``a restriction.''

        24.j   RM83-13.1(10) tries to pretend that representation_clauses
        don't affect the semantics of the program.  One counter-example is
        the Small clause.  Ada 9X has more counter-examples.  We have noted
        the opposite above.

        24.k   Some of the more stringent requirements are moved to C.2,
        ``Required Representation Support''.



13.2 Pragma Pack

1   [A pragma Pack specifies that storage minimization should be the main
criterion when selecting the representation of a composite type.]


                                   Syntax

    2   The form of a pragma Pack is as follows:


3     pragma Pack(first_subtype_local_name);


                               Legality Rules

4   The first_subtype_local_name of a pragma Pack shall denote a composite
subtype.


                              Static Semantics

5   {representation pragma [Pack]} {pragma, representation [Pack]} {aspect of
representation [packing]} {packing (aspect of representation)} {packed} A
pragma Pack specifies the packing aspect of representation; the type (or the
extension part) is said to be packed.  For a type extension, the parent part
is packed as for the parent type, and a pragma Pack causes packing only of
the extension part.

        5.a   Ramification:  The only high level semantic effect of a pragma
        Pack is independent addressability (see 9.10, ``Shared Variables'').


                            Implementation Advice

6   If a type is packed, then the implementation should try to minimize
storage allocated to objects of the type, possibly at the expense of speed of
accessing components, subject to reasonable complexity in addressing
calculations.

        6.a   Ramification:  A pragma Pack is for gaining space efficiency,
        possibly at the expense of time.  If more explicit control over
        representation is desired, then a record_representation_clause, a
        Component_Size clause, or a Size clause should be used instead of, or
        in addition to, a pragma Pack.

7   {recommended level of support [pragma Pack]} The recommended level of
support for pragma Pack is:

    8  For a packed record type, the components should be packed as
       tightly as possible subject to the Sizes of the component
       subtypes, and subject to any record_representation_clause that
       applies to the type; the implementation may, but need not,
       reorder components or cross aligned word boundaries to improve
       the packing.  A component whose Size is greater than the word
       size may be allocated an integral number of words.  {94-4856.a}
       {94-4860.a} {94-4863.a} {94-4885.a} {94-4893.b}

 8.a    Ramification:  The implementation can always allocate an
        integral number of words for a component that will not fit in a
        word.  The rule also allows small component sizes to be rounded
        up if such rounding does not waste space.  For example, if
        Storage_Unit = 8, then a component of size 8 is probably more
        efficient than a component of size 7 plus a 1-bit gap (assuming
        the gap is needed anyway).

    9  For a packed array type, if the component subtype's Size is less
       than or equal to the word size, and Component_Size is not
       specified for the type, Component_Size should be less than or
       equal to the Size of the component subtype, rounded up to the
       nearest factor of the word size.

 9.a    Ramification:  If a component subtype is aliased, its Size will
        generally be a multiple of Storage_Unit, so it probably won't
        get packed very tightly.



13.3 Representation Attributes

1   [{representation attribute} {attribute (representation)} The values of
certain implementation-dependent characteristics can be obtained by
interrogating appropriate representation attributes.  {attribute (specifying)
[distributed]} Some of these attributes are specifiable via an attribute_
definition_clause.]


                         Language Design Principles

        1.a   In general, the meaning of a given attribute should not depend
        on whether the attribute was specified via an attribute_definition_
        clause, or chosen by default by the implementation.

                                   Syntax

2   attribute_definition_clause ::=
          for local_name'attribute_designator use expression;
        | for local_name'attribute_designator use name;


                            Name Resolution Rules

3   For an attribute_definition_clause that specifies an attribute that
denotes a value, the form with an expression shall be used.  Otherwise, the
form with a name shall be used.

4   {expected type [attribute_definition_clause expression or name]} For an
attribute_definition_clause that specifies an attribute that denotes a value
or an object, the expected type for the expression or name is that of the
attribute.

        4.a   Ramification:  For example, the Size attribute is of type
        universal_integer.  Therefore, the expected type for Y in ``for
        X'Size use Y;'' is universal_integer, which means that Y can be of
        any integer type.

{expected profile [attribute_definition_clause name]} For an attribute_
definition_clause that specifies an attribute that denotes a subprogram, the
expected profile for the name is the profile required for the attribute.

        4.b   Discussion:  The required profile is indicated separately for
        the individual attributes.

For an attribute_definition_clause that specifies an attribute that denotes
some other kind of entity, the name shall resolve to denote an entity of the
appropriate kind.

        4.c   Ramification:  For an attribute_definition_clause with a name,
        the name need not statically denote the entity it denotes.  For
        example, the following kinds of things are allowed:

4.d         for Some_Access_Type'Storage_Pool use Storage_Pool_Array(I);
            for Some_Type'Read use Subprogram_Pointer.all;


                               Legality Rules

5   {specifiable (of an attribute and for an entity) [distributed]}
{attribute (specifiable) [distributed]} An attribute_designator is allowed in
an attribute_definition_clause only if this International Standard explicitly
allows it, or for an implementation-defined attribute if the implementation
allows it.  {aspect of representation [specifiable attributes]} Each
specifiable attribute constitutes an aspect of representation.

        5.a   Discussion:  For each specifiable attribute, we generally say
        something like, ``The ... attribute may be specified for ... via an
        attribute_definition_clause.''

        5.b   The above wording allows for T'Class'Alignment, T'Class'Size,
        T'Class'Input, and T'Class'Output to be specifiable.

        5.c   A specifiable attribute is not necessarily specifiable for all
        entities for which it is defined.  For example, one is allowed to ask
        T'Component_Size for an array subtype T, but ``for T'Component_Size
        use ...''  is only allowed if T is a first subtype, because
        Component_Size is a type-related aspect.

6   For an attribute_definition_clause that specifies an attribute that
denotes a subprogram, the profile shall be mode conformant with the one
required for the attribute, and the convention shall be Ada.  Additional
requirements are defined for particular attributes.  {94-4774.b} {subtype
conformance (required)}

        6.a   Ramification:  This implies, for example, that if one writes:

6.b         for T'Read use R;

        6.c   R has to be a procedure with two parameters with the
        appropriate subtypes and modes as shown in 13.13.2.


                              Static Semantics

7   {Address clause} {Alignment clause} {Size clause} {Component_Size clause}
{External_Tag clause} {Small clause} {Bit_Order clause} {Storage_Pool clause}
{Storage_Size clause} {Read clause} {Write clause} {Input clause} {Output
clause} {Machine_Radix clause} A Size clause is an attribute_definition_
clause whose attribute_designator is Size.  Similar definitions apply to the
other specifiable attributes.

        7.a   To be honest:  {type-related [attribute_definition_clause]}
        {subtype-specific [attribute_definition_clause]} An attribute_
        definition_clause is type-related or subtype-specific if the
        attribute_designator denotes a type-related or subtype-specific
        attribute, respectively.

8   {storage element} {byte: see storage element} A storage element is an
addressable element of storage in the machine.  {word} A word is the largest
amount of storage that can be conveniently and efficiently manipulated by the
hardware, given the implementation's run-time model.  A word consists of an
integral number of storage elements.

        8.a   Discussion:  A storage element is not intended to be a single
        bit, unless the machine can efficiently address individual bits.
        8.b   Ramification:  For example, on a machine with 8-bit storage
        elements, if there exist 32-bit integer registers, with a full set of
        arithmetic and logical instructions to manipulate those registers, a
        word ought to be 4 storage elements -- that is, 32 bits.

        8.c   Discussion:  The ``given the implementation's run-time model''
        part is intended to imply that, for example, on an 80386 running
        MS-DOS, the word might be 16 bits, even though the hardware can
        support 32 bits.

        8.d   A word is what ACID refers to as a ``natural hardware
        boundary''.

        8.e   Storage elements may, but need not be, independently
        addressable (see 9.10, ``Shared Variables'').  Words are expected to
        be independently addressable.

9   The following attributes are defined:

10   For a prefix X that denotes an object, program unit, or label:

11  X'Address
                Denotes the address of the first of the storage elements
                allocated to X. For a program unit or label, this value
                refers to the machine code associated with the corresponding
                body or statement.  The value of this attribute is of type
                System.Address.

        11.a   Ramification:  Here, the ``first of the storage elements'' is
        intended to mean the one with the lowest address; the endianness of
        the machine doesn't matter.

                12   {specifiable [of Address for stand-alone objects and for
                program units]} {Address clause} Address may be specified for
                [stand-alone] objects and for program units via an attribute_
                definition_clause.

12.a    Ramification:  Address is not allowed for enumeration literals,
        predefined operators, derived task types, or derived protected types,
        since they are not program units.

12.b    The validity of a given address depends on the run-time model; thus,
        in order to use Address clauses correctly, one needs intimate
        knowledge of the run-time model.

12.c    If the Address of an object is specified, any explicit or implicit
        initialization takes place as usual, unless a pragma Import is also
        specified for the object (in which case any necessary initialization
        is presumably done in the foreign language).

12.d    Any compilation unit containing an attribute_reference of a given
        type depends semantically on the declaration of the package in which
        the type is declared, even if not mentioned in an applicable with_
        clause -- see 10.1.1.  In this case, it means that if a compilation
        unit contains X'Address, then it depends on the declaration of
        System.  Otherwise, the fact that the value of Address is of a type
        in System wouldn't make sense; it would violate the ``legality
        determinable via semantic dependences'' Language Design Principle.

12.e    AI-00305 -- If X is a task type, then within the body of X, X denotes
        the current task object; thus, X'Address denotes the object's
        address.

12.f    Interrupt entries and their addresses are described in J.7.1,
        ``Interrupt Entries''.

12.g    If X is not allocated on a storage element boundary, X'Address points
        at the first of the storage elements that contains any part of
        X. This is important for the definition of the Position attribute to
        be sensible.


                             Erroneous Execution

13   {erroneous execution} If an Address is specified, it is the programmer's
responsibility to ensure that the address is valid; otherwise, program
execution is erroneous.


                            Implementation Advice

14   For an array X, X'Address should point at the first component of the
array, and not at the array bounds.

        14.a   Ramification:  On the other hand, we have no advice to offer
        about discriminants and tag fields; whether or not the address points
        at them is not specified by the language.  If discriminants are
        stored separately, then the Position of a discriminant might be
        negative, or might raise an exception.

15   {recommended level of support [Address attribute]} The recommended level
of support for the Address attribute is:

   16  X'Address should produce a useful result if X is an object that
       is aliased or of a by-reference type, or is an entity whose
       Address has been specified.

 16.a   Reason:  Aliased objects are the ones for which the Unchecked_
        Access attribute is allowed; hence, these have to be allocated
        on an addressable boundary anyway.  Similar considerations apply
        to objects of a by-reference type.

 16.b   An implementation need not go to any trouble to make Address
        work in other cases.  For example, if an object X is not aliased
        and not of a by-reference type, and the implementation chooses
        to store it in a register, X'Address might return System.Null_
        Address (assuming registers are not addressable).  For a
        subprogram whose calling convention is Intrinsic, or for a
        package, the implementation need not generate an out-of-line
        piece of code for it.

   17  An implementation should support Address clauses for imported
       subprograms.

   18  Objects (including subcomponents) that are aliased or of a
       by-reference type should be allocated on storage element
       boundaries.

 18.a   Reason:  This is necessary for the Address attribute to be
        useful (since First_Bit and Last_Bit apply only to components).
        Implementations generally need to do this anyway, for tasking to
        work properly.

   19  If the Address of an object is specified, or it is imported or
       exported, then the implementation should not perform optimiza-
       tions based on assumptions of no aliases.


     NOTES
20   (1) The specification of a link name in a pragma Export (see B.1) for a
     subprogram or object is an alternative to explicit specification of its
     link-time address, allowing a link-time directive to place the
     subprogram or object within memory.

21   (2) The rules for the Size attribute imply, for an aliased object X,
     that if X'Size = Storage_Unit, then X'Address points at a storage
     element containing all of the bits of X, and only the bits of X.


                         Wording Changes From Ada 83

        21.a   The intended meaning of the various attributes, and their
        attribute_definition_clauses, is more explicit.

        21.b   The address_clause has been renamed to at_clause and moved to
        Annex J, ``Obsolescent Features''.  One can use an Address clause
        (``for T'Address use ...;'') instead.

        21.c   The attributes defined in RM83-13.7.3 are moved to Annex G,
        A.5.3, and A.5.4.

                         Language Design Principles

        21.d   By default, the Alignment of a subtype should reflect the
        ``natural'' alignment for objects of the subtype on the machine.  The
        Alignment, whether specified or default, should be known at compile
        time, even though Addresses are generally not known at compile time.
        (The generated code should never need to check at run time the number
        of zero bits at the end of an address to determine an alignment).

        21.e   There are two symmetric purposes of Alignment clauses,
        depending on whether or not the implementation has control over
        object allocation.  If the implementation allocates an object, the
        implementation should ensure that the Address and Alignment are
        consistent with each other.  If something outside the implementation
        allocates an object, the implementation should be allowed to assume
        that the Address and Alignment are consistent, but should not assume
        stricter alignments than that.

                              Static Semantics

22   For a prefix X that denotes a subtype or object:

23  X'Alignment
                The Address of an object that is allocated under control of
                the implementation is an integral multiple of the Alignment
                of the object (that is, the Address modulo the Alignment is
                zero).  The offset of a record component is a multiple of the
                Alignment of the component.  For an object that is not
                allocated under control of the implementation (that is, one
                that is imported, that is allocated by a user-defined
                allocator, whose Address has been specified, or is designated
                by an access value returned by an instance of Unchecked_
                Conversion), the implementation may assume that the Address
                is an integral multiple of its Alignment.  The implementation
                shall not assume a stricter alignment.

                24   The value of this attribute is of type universal_
                integer, and nonnegative; zero means that the object is not
                necessarily aligned on a storage element boundary.

        24.a   Ramification:  The Alignment is passed by an allocator to the
        Allocate operation; the implementation has to choose a value such
        that if the address returned by Allocate is aligned as requested, the
        generated code can correctly access the object.

        24.b   The above mention of ``modulo'' is referring to the "mod"
        operator declared in System.Storage_Elements; if X mod N = 0, then X
        is by definition aligned on an N-storage-element boundary.
        {94-4768.n} {94-4822.a} {94-4825.a} {94-4835.a} {94-4909.a}

                25   {specifiable [of Alignment for first subtypes and
                objects]} {Alignment clause} Alignment may be specified for
                first subtypes and [stand-alone] objects via an attribute_
                definition_clause; the expression of such a clause shall be
                static, and its value nonnegative.  If the Alignment of a
                subtype is specified, then the Alignment of an object of the
                subtype is at least as strict, unless the object's Alignment
                is also specified.  The Alignment of an object created by an
                allocator is that of the designated subtype.

                26   If an Alignment is specified for a composite subtype or
                object, this Alignment shall be equal to the least common
                multiple of any specified Alignments of the subcomponent
                subtypes, or an integer multiple thereof.


                             Erroneous Execution

27   {erroneous execution} Program execution is erroneous if an Address
clause is given that conflicts with the Alignment.

        27.a   Ramification:  The user has to either give an Alignment clause
        also, or else know what Alignment the implementation will choose by
        default.

28   If the Alignment is specified for an object that is not allocated under
control of the implementation, execution is erroneous if the object is not
aligned according to the Alignment.


                            Implementation Advice

29   {recommended level of support [Alignment attribute for subtypes]} The
recommended level of support for the Alignment attribute for subtypes is:

   30  An implementation should support specified Alignments that are
       factors and multiples of the number of storage elements per word,
       subject to the following:

   31  An implementation need not support specified Alignments for
       combinations of Sizes and Alignments that cannot be easily loaded
       and stored by available machine instructions.

   32  An implementation need not support specified Alignments that are
       greater than the maximum Alignment the implementation ever
       returns by default.

33   {recommended level of support [Alignment attribute for objects]} The
recommended level of support for the Alignment attribute for objects is:

   34  Same as above, for subtypes, but in addition:

   35  For stand-alone library-level objects of statically constrained
       subtypes, the implementation should support all Alignments
       supported by the target linker.  For example, page alignment is
       likely to be supported for such objects, but not for subtypes.


     NOTES
36   (3) Alignment is a subtype-specific attribute.

37   (4) The Alignment of a composite object is always equal to the least
     common multiple of the Alignments of its components, or a multiple
     thereof.

   37.a   Discussion:  For default Alignments, this follows from the
        semantics of Alignment.  For specified Alignments, it follows from a
        Legality Rule stated above.

38   (5) A component_clause, Component_Size clause, or a pragma Pack can
     override a specified Alignment.

   38.a   Discussion:  Most objects are allocated by the implementation; for
        these, the implementation obeys the Alignment.  The implementation is
        of course allowed to make an object more aligned than its Alignment
        requires -- an object whose Alignment is 4 might just happen to land
        at an address that's a multiple of 4096.  For formal parameters, the
        implementation might want to force an Alignment stricter than the
        parameter's subtype.  For example, on some systems, it is customary
        to always align parameters to 4 storage elements.

   38.b   Hence, one might initially assume that the implementation could
        evilly make all Alignments 1 by default, even though integers, say,
        are normally aligned on a 4-storage-element boundary.  However, the
        implementation cannot get away with that -- if the Alignment is 1,
        the generated code cannot assume an Alignment of 4, at least not for
        objects allocated outside the control of the implementation.

   38.c   Of course implementations can assume anything they can prove, but
        typically an implementation will be unable to prove much about the
        alignment of, say, an imported object.  Furthermore, the information
        about where an address ``came from'' can be lost to the compiler due
        to separate compilation.

   38.d   The Alignment of an object that is a component of a packed
        composite object will usually be 0, to indicate that the component is
        not necessarily aligned on a storage element boundary.  For a
        subtype, an Alignment of 0 means that objects of the subtype are not
        normally aligned on a storage element boundary at all.  For example,
        an implementation might choose to make Component_Size be 0 for an
        array of Booleans, even when pragma Pack has not been specified for
        the array.  In this case, Boolean'Alignment would be 0.  (In the
        presence of tasking, this would in general be feasible only on a
        machine that had atomic test-bit and set-bit instructions.)

   38.e   If the machine has no particular natural alignments, then all
        subtype Alignments will probably be 1 by default.

   38.f   Specifying an Alignment of 0 in an attribute_definition_clause does
        not require the implementation to do anything (except return 0 when
        the Alignment is queried).  However, it might be taken as advice on
        some implementations.

   38.g   It is an error for an Address clause to disobey the object's
        Alignment.  The error cannot be detected at compile time, in general,
        because the Address is not necessarily known at compile time (and is
        almost certainly not static).  We do not require a run-time check,
        since efficiency seems paramount here, and Address clauses are
        treading on thin ice anyway.  Hence, this misuse of Address clauses
        is just like any other misuse of Address clauses -- it's erroneous.

   38.h   A type extension can have a stricter Alignment than its parent.
        This can happen, for example, if the Alignment of the parent is 4,
        but the extension contains a component with Alignment 8.  The
        Alignment of a class-wide type or object will have to be the maximum
        possible Alignment of any extension.

   38.i   The recommended level of support for the Alignment attribute is
        intended to reflect a minimum useful set of capabilities.  An
        implementation can assume that all Alignments are multiples of each
        other -- 1, 2, 4, and 8 might be the only supported Alignments for
        subtypes.  An Alignment of 3 or 6 is unlikely to be useful.  For
        objects that can be allocated statically, we recommend that the
        implementation support larger alignments, such as 4096.  We do not
        recommend such large alignments for subtypes, because the maximum
        subtype alignment will also have to be used as the alignment of stack
        frames, heap objects, and class-wide objects.  Similarly, we do not
        recommend such large alignments for stack-allocated objects.

   38.j   If the maximum default Alignment is 8 (say, Long_Float'Alignment =
        8), then the implementation can refuse to accept stricter alignments
        for subtypes.  This simplifies the generated code, since the compiler
        can align the stack and class-wide types to this maximum without a
        substantial waste of space (or time).

   38.k   Note that the recommended level of support takes into account
        interactions between Size and Alignment.  For example, on a 32-bit
        machine with 8-bit storage elements, where load and store
        instructions have to be aligned according to the size of the thing
        being loaded or stored, the implementation might accept an Alignment
        of 1 if the Size is 8, but might reject an Alignment of 1 if the Size
        is 32.  On a machine where unaligned loads and stores are merely
        inefficient (as opposed to causing hardware traps), we would expect
        an Alignment of 1 to be supported for any Size.


                         Wording Changes From Ada 83

        38.l   The nonnegative part is missing from RM83 (for mod_clauses,
        nee alignment_clauses, which are an obsolete version of Alignment
        clauses).

                              Static Semantics

39   For a prefix X that denotes an object:

40  X'Size
                Denotes the size in bits of the representation of the object.
                The value of this attribute is of the type universal_integer.

        40.a   Ramification:  Note that Size is in bits even if Machine_Radix
        is 10.  Each decimal digit (and the sign) is presumably represented
        as some number of bits.

                41   {specifiable [of Size for stand-alone objects]} {Size
                clause} Size may be specified for [stand-alone] objects via
                an attribute_definition_clause; the expression of such a
                clause shall be static and its value nonnegative.


                            Implementation Advice

42   {recommended level of support [Size attribute]} The recommended level of
support for the Size attribute of objects is:

   43  A Size clause should be supported for an object if the specified
       Size is at least as large as its subtype's Size, and corresponds
       to a size in storage elements that is a multiple of the object's
       Alignment (if the Alignment is nonzero).


                              Static Semantics

44   For every subtype S:

45  S'Size
                If S is definite, denotes the size [(in bits)] that the
                implementation would choose for the following objects of
                subtype S:
                   46  A record component of subtype S when the record
                       type is packed.

                   47  The formal parameter of an instance of Unchecked_
                       Conversion that converts from subtype S to some
                       other subtype.

                48   If S is indefinite, the meaning is implementation
                defined.  The value of this attribute is of the type
                universal_integer.  {specifiable [of Size for first
                subtypes]} {Size clause} The Size of an object is at least as
                large as that of its subtype, unless the object's Size is
                determined by a Size clause, a component_clause, or a
                Component_Size clause.  {94-4856.a} {94-4860.a} {94-4863.a}
                {94-4885.a} {94-4893.b} Size may be specified for first
                subtypes via an attribute_definition_clause; the expression
                of such a clause shall be static and its value nonnegative.

48.a    Implementation defined:  The meaning of Size for indefinite subtypes.

48.b    Reason:  The effects of specifying the Size of a subtype are:

         48.c  Unchecked_Conversion works in a predictable manner.

         48.d  A composite type cannot be packed so tightly as to
               override the specified Size of a component's subtype.

         48.e  Assuming the Implementation Advice is obeyed, if the
               specified Size allows independent addressability, then
               the Size of certain objects of the subtype should be
               equal to the subtype's Size.  This applies to stand-alone
               objects and to components (unless a component_clause or a
               Component_Size clause applies).

48.f    A component_clause or a Component_Size clause can cause an object to
        be smaller than its subtype's specified size.  A pragma Pack cannot;
        if a component subtype's size is specified, this limits how tightly
        the composite object can be packed.

48.g    The Size of a class-wide (tagged) subtype is unspecified, because
        it's not clear what it should mean; it should certainly not depend on
        all of the descendants that happen to exist in a given program.  Note
        that this cannot be detected at compile time, because in a generic
        unit, it is not necessarily known whether a given subtype is
        class-wide.  It might raise an exception on some implementations.

48.h    Ramification:  A Size clause for a numeric subtype need not affect
        the underlying numeric type.  For example, if I say:

48.i        type S is range 1..2;
            for S'Size use 64;

48.j    I am not guaranteed that S'Base'Last >= 2**63-1, nor that
        intermediate results will be represented in 64 bits.

48.k    Reason:  There is no need to complicate implementations for this sort
        of thing, because the right way to affect the base range of a type is
        to use the normal way of declaring the base range:

48.l        type Big is range -2**63 .. 2**63 - 1;
            subtype Small is Big range 1..1000;

48.m    Ramification:  The Size of a large unconstrained subtype (e.g.
        String'Size) is likely to raise Constraint_Error, since it is a
        nonstatic expression of type universal_integer that might overflow
        the largest signed integer type.  There is no requirement that the
        largest integer type be able to represent the size in bits of the
        largest possible object.


                         Implementation Requirements

49   In an implementation, Boolean'Size shall be 1.  {94-4776.e}


                            Implementation Advice

50   If the Size of a subtype is specified, and allows for efficient
independent addressability (see 9.10) on the target architecture, then the
Size of the following objects of the subtype should equal the Size of the
subtype:

   51  Aliased objects (including components).

   52  Unaliased components, unless the Size of the component is
       determined by a component_clause or Component_Size clause.
       {94-4856.a} {94-4860.a} {94-4863.a} {94-4885.a} {94-4893.b}

        52.a   Ramification:  Thus, on a typical 32-bit machine, ``for S'Size
        use 32;'' will guarantee that aliased objects of subtype S, and
        components whose subtype is S, will have Size = 32 (assuming the
        implementation chooses to obey this Implementation Advice).  On the
        other hand, if one writes, ``for S2'Size use 5;'' then stand-alone
        objects of subtype S2 will typically have their Size rounded up to
        ensure independent addressability.

        52.b   Note that ``for S'Size use 32;'' does not cause things like
        formal parameters to have Size = 32 -- the implementation is allowed
        to make all parameters be at least 64 bits, for example.

        52.c   Note that ``for S2'Size use 5;'' requires record components
        whose subtype is S2 to be exactly 5 bits if the record type is
        packed.  The same is not true of array components; their Size may be
        rounded up to the nearest factor of the word size.

        52.d   Implementation Note:  {gaps} On most machines, arrays don't
        contain gaps between components; if the Component_Size is greater
        than the Size of the component subtype, the extra bits are generally
        considered part of each component, rather than gaps between
        components.  On the other hand, a record might contain gaps between
        components, depending on what sorts of loads, stores, and masking
        operations are generally done by the generated code.

        52.e   For an array, any extra bits stored for each component will
        generally be part of the component -- the whole point of storing
        extra bits is to make loads and stores more efficient by avoiding the
        need to mask out extra bits.  The PDP-10 is one counter-example;
        since the hardware supports byte strings with a gap at the end of
        each word, one would want to pack in that manner.

53   A Size clause on a composite subtype should not affect the internal
layout of components.

        53.a   Reason:  That's what Pack pragmas, record_representation_
        clauses, and Component_Size clauses are for.

54   {recommended level of support [Size attribute]} The recommended level of
support for the Size attribute of subtypes is:

   55  The Size (if not specified) of a static discrete or fixed point
       subtype should be the number of bits needed to represent each
       value belonging to the subtype using an unbiased representation,
       leaving space for a sign bit only if the subtype contains
       negative values.  If such a subtype is a first subtype, then an
       implementation should support a specified Size for it that
       reflects this representation.  {94-4856.a} {94-4860.a}
       {94-4863.a} {94-4885.a} {94-4893.b}

 55.a   Implementation Note:  This applies to static enumeration
        subtypes, using the internal codes used to represent the values.

 55.b   For a two's-complement machine, this implies that for a static
        signed integer subtype S, if all values of S are in the range 0
            n                                          n-1     n-1
        .. 2 -1, or all values of S are in the range -2    .. 2   -1,
        for some n less than or equal to the word size, then S'Size
        should be <= the smallest such n.  For a one's-complement
        machine, it is the same except that in the second range, the
                        n-1                      n-1
        lower bound ``-2   '' is replaced by ``-2   +1''.

 55.c   If an integer subtype (whether signed or unsigned) contains no
        negative values, the Size should not include space for a sign
        bit.

 55.d   Typically, the implementation will choose to make the Size of a
        subtype be exactly the smallest such n.  However, it might, for
        example, choose a biased representation, in which case it could
        choose a smaller value.

 55.e   On most machines, it is in general not a good idea to pack
        (parts of) multiple stand-alone objects into the same storage
        element, because (1) it usually doesn't save much space, and (2)
        it requires locking to prevent tasks from interfering with each
        other, since separate stand-alone objects are independently
        addressable.  Therefore, if S'Size = 2 on a machine with 8-bit
        storage elements, the size of a stand-alone object of subtype S
        will probably not be 2.  It might, for example, be 8, 16 or 32,
        depending on the availability and efficiency of various machine
        instructions.  The same applies to components of composite
        types, unless packing, Component_Size, or record layout is
        specified.

 55.f   For an unconstrained discriminated object, if the implementation
        allocates the maximum possible size, then the Size attribute
        should return that maximum possible size.

 55.g   Ramification:  The Size of an object X is not usually the same
        as that of its subtype S. If X is a stand-alone object or a
        parameter, for example, most implementations will round X'Size
        up to a storage element boundary, or more, so X'Size might be
        greater than S'Size.  On the other hand, X'Size cannot be less
        than S'Size, even if the implementation can prove, for example,
        that the range of values actually taken on by X during execution
        is smaller than the range of S.

 55.h   For example, if S is a first integer subtype whose range is
        0..3, S'Size will be probably be 2 bits, and components of
        packed composite types of this subtype will be 2 bits (assuming
        Storage_Unit is a multiple of 2), but stand-alone objects and
        parameters will probably not have a size of 2 bits; they might
        be rounded up to 32 bits, for example.  On the other hand,
        Unchecked_Conversion will use the 2-bit size, even when
        converting a stand-alone object, as one would expect.

 55.i   Another reason for making the Size of an object bigger than its
        subtype's Size is to support the run-time detection of
        uninitialized variables.  {uninitialized variables [partial]}
        The implementation might add an extra value to a discrete
        subtype that represents the uninitialized state, and check for
        this value on use.  In some cases, the extra value will require
        an extra bit in the representation of the object.  Such
        detection is not required by the language.  If it is provided,
        the implementation has to be able to turn it off.  For example,
        if the programmer gives a record_representation_clause or
        Component_Size clause that makes a component too small to allow
        the extra bit, then the implementation will not be able to
        perform the checking (not using this method, anyway).

 55.j   The fact that the size of an object is not necessarily the same
        as its subtype can be confusing:

55.k        type Device_Register is range 0..2**8 - 1;
            for Device_Register'Size use 8; -- Confusing!
            My_Device : Device_Register;
            for My_Device'Address use To_Address(16#FF00#);

 55.l   The programmer might think that My_Device'Size is 8, and that
        My_Device'Address points at an 8-bit location.  However, this is
        not true.  In Ada 83 (and in Ada 9X), My_Device'Size might well
        be 32, and My_Device'Address might well point at the high-order
        8 bits of the 32-bit object, which are always all zero bits.  If
        My_Device'Address is passed to an assembly language subprogram,
        based on the programmer's assumption, the program will not work
        properly.

 55.m   Reason:  It is not reasonable to require that an implementation
        allocate exactly 8 bits to all objects of subtype Device_
        Register.  For example, in many run-time models, stand-alone
        objects and parameters are always aligned to a word boundary.
        Such run-time models are generally based on hardware
        considerations that are beyond the control of the implementer.
        (It is reasonable to require that an implementation allocate
        exactly 8 bits to all components of subtype Device_Register, if
        packed.)

 55.n   Ramification:  The correct way to write the above code is like
        this:

55.o        type Device_Register is range 0..2**8 - 1;
            My_Device : Device_Register;
            for My_Device'Size use 8;
            for My_Device'Address use To_Address(16#FF00#);

 55.p   If the implementation cannot accept 8-bit stand-alone objects,
        then this will be illegal.  However, on a machine where an 8-bit
        device register exists, the implementation will probably be able
        to accept 8-bit stand-alone objects.  Therefore, My_Device'Size
        will be 8, and My_Device'Address will point at those 8 bits, as
        desired.

 55.q   If an object of subtype Device_Register is passed to a foreign
        language subprogram, it will be passed according to that
        subprogram's conventions.  Most foreign language implementations
        have similar run-time model restrictions.  For example, when
        passing to a C function, where the argument is of the C type
        char* (that is, pointer to char), the C compiler will generally
        expect a full word value, either on the stack, or in a register.
        It will not expect a single byte.  Thus, Size clauses for
        subtypes really have nothing to do with passing parameters to
        foreign language subprograms.

   56  For a subtype implemented with levels of indirection, the Size
       should include the size of the pointers, but not the size of what
       they point at.

 56.a   Ramification:  For example, if a task object is represented as a
        pointer to some information (including a task stack), then the
        size of the object should be the size of the pointer.  The
        Storage_Size, on the other hand, should include the size of the
        stack.


     NOTES
57   (6) Size is a subtype-specific attribute.

58   (7) A component_clause or Component_Size clause can override a specified
     Size.  A pragma Pack cannot.


                         Wording Changes From Ada 83

        58.a   The requirement for a nonnegative value in a Size clause was
        not in RM83, but it's hard to see how it would make sense.  For
        uniformity, we forbid negative sizes, rather than letting
        implementations define their meaning.

                              Static Semantics

59   For a prefix T that denotes a task object [(after any implicit
dereference)]:

60  T'Storage_Size
                Denotes the number of storage elements reserved for the task.
                The value of this attribute is of the type universal_integer.
                The Storage_Size includes the size of the task's stack, if
                any.  The language does not specify whether or not it
                includes other storage associated with the task (such as the
                ``task control block'' used by some implementations.)  If a
                pragma Storage_Size is given, the value of the Storage_Size
                attribute is at least the value specified in the pragma.

60.a    Ramification:  The value of this attribute is never negative, since
        it is impossible to ``reserve'' a negative number of storage
        elements.

60.b    If the implementation chooses to allocate an initial amount of
        storage, and then increase this as needed, the Storage_Size cannot
        include the additional amounts (assuming the allocation of the
        additional amounts can raise Storage_Error); this is inherent in the
        meaning of ``reserved.''

60.c    The implementation is allowed to allocate different amounts of
        storage for different tasks of the same subtype.

60.d    Storage_Size is also defined for access subtypes -- see 13.11.


61   [{Storage_Size clause: see also pragma Storage_Size} A pragma Storage_
Size specifies the amount of storage to be reserved for the execution of a
task.]


                                   Syntax

    62   The form of a pragma Storage_Size is as follows:


63    pragma Storage_Size(expression);

    64   A pragma Storage_Size is allowed only immediately within a task_
    definition.


                            Name Resolution Rules

65   {expected type [Storage_Size pragma argument]} The expression of a
pragma Storage_Size is expected to be of any integer type.


                              Dynamic Semantics

66   A pragma Storage_Size is elaborated when an object of the type defined
by the immediately enclosing task_definition is created.  {elaboration
[Storage_Size pragma]} For the elaboration of a pragma Storage_Size, the
expression is evaluated; the Storage_Size attribute of the newly created task
object is at least the value of the expression.

        66.a   Ramification:  The implementation is allowed to round up a
        specified Storage_Size amount.  For example, if the implementation
        always allocates in chunks of 4096 bytes, the number 200 might be
        rounded up to 4096.  Also, if the user specifies a negative number,
        the implementation has to normalize this to 0, or perhaps to a
        positive number.

67   {Storage_Check [partial]} {check, language-defined (Storage_Check)}
{Storage_Error (raised by failure of run-time check)} At the point of task
object creation, or upon task activation, Storage_Error is raised if there is
insufficient free storage to accommodate the requested Storage_Size.


                              Static Semantics

68   For a prefix X that denotes an array subtype or array object [(after any
implicit dereference)]:

69  X'Component_Size
                Denotes the size in bits of components of the type of X. The
                value of this attribute is of type universal_integer.

                70   {specifiable [of Component_Size for array types]}
                {Component_Size clause} Component_Size may be specified for
                array types via an attribute_definition_clause; the
                expression of such a clause shall be static, and its value
                nonnegative.

        70.a   Implementation Note:  The intent is that the value of
        X'Component_Size is always nonnegative.  If the array is stored
        ``backwards'' in memory (which might be caused by an implementation-
        defined pragma), X'Component_Size is still positive.

70.b    Ramification:  For an array object A, A'Component_Size = A(I)'Size
        for any index I.


                            Implementation Advice

71   {recommended level of support [Component_Size attribute]} The
recommended level of support for the Component_Size attribute is:

   72  An implementation need not support specified Component_Sizes that
       are less than the Size of the component subtype.

   73  An implementation should support specified Component_Sizes that
       are factors and multiples of the word size.  For such Component_
       Sizes, the array should contain no gaps between components.  For
       other Component_Sizes (if supported), the array should contain no
       gaps between components when packing is also specified; the
       implementation should forbid this combination in cases where it
       cannot support a no-gaps representation.
 73.a   Ramification:  For example, if Storage_Unit = 8, and Word_Size =
        32, then the user is allowed to specify a Component_Size of 1,
        2, 4, 8, 16, and 32, with no gaps.  In addition, n*32 is allowed
        for positive integers n, again with no gaps.  If the
        implementation accepts Component_Size = 3, then it might
        allocate 10 components per word, with a 2-bit gap at the end of
        each word (unless packing is also specified), or it might not
        have any internal gaps at all.  (There can be gaps at either end
        of the array.)


                              Static Semantics

74   For every subtype S of a tagged type T (specific or class-wide), the
following attribute is defined:

75  S'External_Tag
                {External_Tag clause} {specifiable [of External_Tag for a
                tagged type]} S'External_Tag denotes an external string
                representation for S'Tag; it is of the predefined type
                String.  External_Tag may be specified for a specific tagged
                type via an attribute_definition_clause; the expression of
                such a clause shall be static.  The default external tag
                representation is implementation defined.  See 3.9.2 and
                13.13.2.

75.a    Implementation defined:  The default external representation for a
        type tag.


                         Implementation Requirements

76   In an implementation, the default external tag for each specific tagged
type declared in a partition shall be distinct, so long as the type is
declared outside an instance of a generic body.  If the compilation unit in
which a given tagged type is declared, and all compilation units on which it
semantically depends, are the same in two different partitions, then the
external tag for the type shall be the same in the two partitions.  What it
means for a compilation unit to be the same in two different partitions is
implementation defined.  At a minimum, if the compilation unit is not
recompiled between building the two different partitions that include it, the
compilation unit is considered the same in the two partitions.

        76.a   Implementation defined:  What determines whether a compilation
        unit is the same in two different partitions.

        76.b   Reason:  These requirements are important because external
        tags are used for input/output of class-wide types.  These
        requirements ensure that what is written by one program can be read
        back by some other program so long as they share the same declaration
        for the type (and everything it depends on).

        76.c   The user may specify the external tag if (s)he wishes its
        value to be stable even across changes to the compilation unit in
        which the type is declared (or changes in some unit on which it
        depends).

        76.d   We use a String rather than a Storage_Array to represent an
        external tag for portability.

        76.e   Ramification:  Note that the characters of an external tag
        need not all be graphic characters.  In other words, the external tag
        can be a sequence of arbitrary 8-bit bytes.


     NOTES
77   (8) The following language-defined attributes are specifiable, at least
     for some of the kinds of entities to which they apply:  Address, Size,
     Component_Size, Alignment, External_Tag, Small, Bit_Order, Storage_Pool,
     Storage_Size, Write, Output, Read, Input, and Machine_Radix.

78   (9) It follows from the general rules in 13.1 that if one writes ``for
     X'Size use Y;'' then the X'Size attribute_reference will return Y
     (assuming the implementation allows the Size clause).  The same is true
     for all of the specifiable attributes except Storage_Size.

   78.a   Ramification:  An implementation may specify that an
        implementation-defined attribute is specifiable for certain entities.
        This follows from the fact that the semantics of implementation-
        defined attributes is implementation defined.  An implementation is
        not allowed to make a language-defined attribute specifiable if it
        isn't.


                                  Examples

79   Examples of attribute definition clauses:

80  Byte : constant := 8;
    Page : constant := 2**12;

81  type Medium is range 0 .. 65_000;
    for Medium'Size use 2*Byte;
    for Medium'Alignment use 2;
    Device_Register : Medium;
    for Device_Register'Size use Medium'Size;
    for Device_Register'Address use System.Storage_Elements.To_Address(16#FFFF_\
0020#);

82  type Short is delta 0.01 range -100.0 .. 100.0;
    for Short'Size use 15;

83  for Car_Name'Storage_Size use -- specify access type's storage pool size
            2000*((Car'Size/System.Storage_Unit) +1); -- approximately 2000 cars

84  function My_Read(Stream : access Ada.Streams.Root_Stream_Type'Class)
      return T;
    for T'Read use My_Read; -- see 13.13.2


     NOTES
85   (10) Notes on the examples:  In the Size clause for Short, fifteen bits
     is the minimum necessary, since the type definition requires Short'Small
     <= 2**(-7).


                            Extensions to Ada 83

        85.a   {extensions to Ada 83} The syntax rule for length_clause is
        replaced with the new syntax rule for attribute_definition_clause,
        and it is modified to allow a name (as well as an expression).

                         Wording Changes From Ada 83

        85.b   The syntax rule for attribute_definition_clause now requires
        that the prefix of the attribute be a local_name; in Ada 83 this rule
        was stated in the text.

        85.c   In Ada 83, the relationship between a representation_clause
        specifying a certain aspect and an attribute that queried that aspect
        was unclear.  In Ada 9X, they are the same, except for certain
        explicit exceptions.



13.4 Enumeration Representation Clauses

1   [An enumeration_representation_clause specifies the internal codes for
enumeration literals.]


                                   Syntax

2   enumeration_representation_clause ::=
        for first_subtype_local_name use enumeration_aggregate;

3   enumeration_aggregate ::= array_aggregate


                            Name Resolution Rules

4   {expected type [enumeration_representation_clause expressions]} The
enumeration_aggregate shall be written as a one-dimensional array_aggregate,
for which the index subtype is the unconstrained subtype of the enumeration
type, and each component expression is expected to be of any integer type.

        4.a   Ramification:  The ``full coverage rules'' for aggregates
        applies.  An others is not allowed -- there is no applicable index
        constraint in this context.


                               Legality Rules

5   The first_subtype_local_name of an enumeration_representation_clause
shall denote an enumeration subtype.

        5.a   Ramification:  As for all type-related representation items,
        the local_name is required to denote a first subtype.

6   The expressions given in the array_aggregate shall be static, and shall
specify distinct integer codes for each value of the enumeration type; the
associated integer codes shall satisfy the predefined ordering relation of
the type.

        6.a   Reason:  Each value of the enumeration type has to be given an
        internal code, even if the first subtype of the enumeration type is
        constrained to only a subrange (this is only possible if the
        enumeration type is a derived type).  This ``full coverage''
        requirement is important because one may refer to Enum'Base'First and
        Enum'Base'Last, which need to have defined representations.


                              Static Semantics

7   {aspect of representation [coding]} {coding (aspect of representation)}
An enumeration_representation_clause specifies the coding aspect of
representation.  {internal code} The coding consists of the internal code for
each enumeration literal, that is, the integral value used internally to
represent each literal.


                         Implementation Requirements

8   For nonboolean enumeration types, if the coding is not specified for the
type, then for each value of the type, the internal code shall be equal to
its position number.

        8.a   Reason:  This default representation is already used by all
        known Ada compilers for nonboolean enumeration types.  Therefore, we
        make it a requirement so users can depend on it, rather than feeling
        obliged to supply for every enumeration type an enumeration
        representation clause that is equivalent to this default rule.

        8.b   Discussion:  For boolean types, it is relatively common to use
        all ones for True, and all zeros for False, since some hardware
        supports that directly.  Of course, for a one-bit Boolean object
        (like in a packed array), False is presumably zero and True is
        presumably one (choosing the reverse would be extremely unfriendly!).


                            Implementation Advice

9   {recommended level of support [enumeration_representation_clause]} The
recommended level of support for enumeration_representation_clauses is:

   10  An implementation should support at least the internal codes in
       the range System.Min_Int..System.Max_Int.  An implementation need
       not support enumeration_representation_clauses for boolean types.

 10.a   Ramification:  The implementation may support numbers outside
        the above range, such as numbers greater than System.Max_Int.
        See AI-00564.

 10.b   Reason:  The benefits of specifying the internal coding of a
        boolean type do not outweigh the implementation costs.
        Consider, for example, the implementation of the logical
        operators on a packed array of booleans with strange internal
        codes.  It's implementable, but not worth it.


     NOTES
11   (11) Unchecked_Conversion may be used to query the internal codes used
     for an enumeration type.  The attributes of the type, such as Succ,
     Pred, and Pos, are unaffected by the representation_clause.  For
     example, Pos always returns the position number, not the internal
     integer code that might have been specified in a representation_clause.

   11.a   Discussion:  Suppose the enumeration type in question is derived:

11.b        type T1 is (Red, Green, Blue);
            subtype S1 is T1 range Red .. Green;
            type S2 is new S1;
            for S2 use (Red => 10, Green => 20, Blue => 30);

   11.c   The representation_clause has to specify values for all enumerals,
        even ones that are not in S2 (such as Blue).  The Base attribute can
        be used to get at these values.  For example:

11.d        for I in S2'Base loop
                ... -- When I equals Blue, the internal code is 30.
            end loop;

   11.e   We considered allowing or requiring ``for S2'Base use ...'' in
        cases like this, but it didn't seem worth the trouble.


                                  Examples

12   Example of an enumeration representation clause:

13  type Mix_Code is (ADD, SUB, MUL, LDA, STA, STZ);

14  for Mix_Code use
       (ADD => 1, SUB => 2, MUL => 3, LDA => 8, STA => 24, STZ =>33);


                            Extensions to Ada 83

        14.a   {extensions to Ada 83} As in other similar contexts, Ada 9X
        allows expressions of any integer type, not just expressions of type
        universal_integer, for the component expressions in the enumeration_
        aggregate.  The preference rules for the predefined operators of
        root_integer eliminate any ambiguity.

        14.b   For portability, we now require that the default coding for an
        enumeration type be the ``obvious'' coding using position numbers.
        This is satisfied by all known implementations.



13.5 Record Layout

1   {aspect of representation [layout]} {layout (aspect of representation)}
{aspect of representation [record layout]} {record layout (aspect of
representation)} {aspect of representation [storage place]} {storage place
(of a component)} The (record) layout aspect of representation consists of
the storage places for some or all components, that is, storage place
attributes of the components.  The layout can be specified with a record_
representation_clause.



13.5.1 Record Representation Clauses

1   [A record_representation_clause specifies the storage representation of
records and record extensions, that is, the order, position, and size of
components (including discriminants, if any).  {bit field: see record_
representation_clause}]


                         Language Design Principles

        1.a   It should be feasible for an implementation to use negative
        offsets in the representation of composite types.  However, no
        implementation should be forced to support negative offsets.
        Therefore, negative offsets should be disallowed in record_
        representation_clauses.

                                   Syntax

2   record_representation_clause ::=
        for first_subtype_local_name use
          record [mod_clause]
            {component_clause}
          end record;

3   component_clause ::=
        component_local_name at position range first_bit .. last_bit;

4   position ::= static_expression

5   first_bit ::= static_simple_expression

6   last_bit ::= static_simple_expression

        6.a   Reason:  First_bit and last_bit need to be simple_expression
        instead of expression for the same reason as in range (see 3.5,
        ``Scalar Types'').


                            Name Resolution Rules

7   {expected type [component_clause expressions]} {expected type [position]}
{expected type [first_bit]} {expected type [last_bit]} Each position, first_
bit, and last_bit is expected to be of any integer type.

        7.a   Ramification:  These need not have the same integer type.


                               Legality Rules

8   The first_subtype_local_name of a record_representation_clause shall
denote a specific nonlimited record or record extension subtype.  {94-4776.f}

        8.a   Ramification:  As for all type-related representation items,
        the local_name is required to denote a first subtype.

9   If the component_local_name is a direct_name, the local_name shall denote
a component of the type.  For a record extension, the component shall not be
inherited, and shall not be a discriminant that corresponds to a discriminant
of the parent type.  If the component_local_name has an attribute_designator,
the direct_name of the local_name shall denote either the declaration of the
type or a component of the type, and the attribute_designator shall denote an
implementation-defined implicit component of the type.

10   The position, first_bit, and last_bit shall be static expressions.  The
value of position and first_bit shall be nonnegative.  The value of last_bit
shall be no less than first_bit - 1.

        10.a   Ramification:  A component_clause such as ``X at 4 range
        0..-1;'' is allowed if X can fit in zero bits.

11   At most one component_clause is allowed for each component of the type,
including for each discriminant (component_clauses may be given for some,
all, or none of the components).  Storage places within a component_list
shall not overlap, unless they are for components in distinct variants of the
same variant_part.

12   A name that denotes a component of a type is not allowed within a
record_representation_clause for the type, except as the component_local_name
of a component_clause.

        12.a   Reason:  It might seem strange to make the record_
        representation_clause part of the declarative region, and then
        disallow mentions of the components within almost all of the record_
        representation_clause.  The alternative would be to treat the
        component_local_name like a formal parameter name in a subprogram
        call (in terms of visibility).  However, this rule would imply
        slightly different semantics, because (given the actual rule) the
        components can hide other declarations.  This was the rule in Ada 83,
        and we see no reason to change it.  The following, for example, was
        and is illegal:

12.b        type T is
                record
                    X : Integer;
                end record;
            X : constant := 31; -- Same defining name as the component.
            for T use
                record
                    X at 0 range 0..X; -- Illegal!
                end record;

        12.c   The component X hides the named number X throughout the
        record_representation_clause.


                              Static Semantics

13   A record_representation_clause (without the mod_clause) specifies the
layout.  The storage place attributes (see 13.5.2) are taken from the values
of the position, first_bit, and last_bit expressions after normalizing those
values so that first_bit is less than Storage_Unit.

        13.a   Ramification:  For example, if Storage_Unit is 8, then ``C at
        0 range 24..31;'' defines C'Position = 3, C'First_Bit = 0, and
        C'Last_Bit = 7.  This is true of machines with either bit ordering.

        13.b   A component_clause also determines the value of the Size
        attribute of the component, since this attribute is related to First_
        Bit and Last_Bit.

14   [A record_representation_clause for a record extension does not override
the layout of the parent part;] if the layout was specified for the parent
type, it is inherited by the record extension.


                         Implementation Permissions

15   An implementation may generate implementation-defined components (for
example, one containing the offset of another component).  An implementation
may generate names that denote such implementation-defined components; such
names shall be implementation-defined attribute_references.  An implemen-
tation may allow such implementation-defined names to be used in record_
representation_clauses.  An implementation can restrict such component_
clauses in any manner it sees fit.

        15.a   Implementation defined:  Implementation-defined components.

        15.b   Ramification:  Of course, since the semantics of
        implementation-defined attributes is implementation defined, the
        implementation need not support these names in all situations.  They
        might be purely for the purpose of component_clauses, for example.
        The visibility rules for such names are up to the implementation.

        15.c   We do not allow such component names to be normal identifiers
        -- that would constitute blanket permission to do all kinds of evil
        things.

        15.d   Discussion:  {dope} Such implementation-defined components are
        known in the vernacular as ``dope.''  Their main purpose is for
        storing offsets of components that depend on discriminants.

16   If a record_representation_clause is given for an untagged derived type,
the storage place attributes for all of the components of the derived type
may differ from those of the corresponding components of the parent type,
even for components whose storage place is not specified explicitly in the
record_representation_clause.

        16.a   Reason:  This is clearly necessary, since the whole record may
        need to be laid out differently.


                            Implementation Advice

17   {recommended level of support [record_representation_clause]} The
recommended level of support for record_representation_clauses is:

   18  An implementation should support storage places that can be
       extracted with a load, mask, shift sequence of machine code, and
       set with a load, shift, mask, store sequence, given the available
       machine instructions and run-time model.

   19  A storage place should be supported if its size is equal to the
       Size of the component subtype, and it starts and ends on a
       boundary that obeys the Alignment of the component subtype.

   20  If the default bit ordering applies to the declaration of a given
       type, then for a component whose subtype's Size is less than the
       word size, any storage place that does not cross an aligned word
       boundary should be supported.

 20.a   Reason:  The above recommendations are sufficient to define
        interfaces to most interesting hardware.  This causes less
        implementation burden than the definition in ACID, which
        requires arbitrary bit alignments of arbitrarily large
        components.  Since the ACID definition is neither enforced by
        the ACVC, nor supported by all implementations, it seems OK for
        us to weaken it.

   21  An implementation may reserve a storage place for the tag field
       of a tagged type, and disallow other components from overlapping
       that place.

 21.a   Ramification:  Similar permission for other dope is not granted.

   22  An implementation need not support a component_clause for a
       component of an extension part if the storage place is not after
       the storage places of all components of the parent type, whether
       or not those storage places had been specified.

 22.a   Reason:  These restrictions are probably necessary if block
        equality operations are to be feasible for class-wide types.
        For block comparison to work, the implementation typically has
        to fill in any gaps with zero (or one) bits.  If a ``gap'' in
        the parent type is filled in with a component in a type
        extension, then this won't work when a class-wide object is
        passed by reference, as is required.


     NOTES
23   (12) If no component_clause is given for a component, then the choice of
     the storage place for the component is left to the implementation.  If
     component_clauses are given for all components, the record_
     representation_clause completely specifies the representation of the
     type and will be obeyed exactly by the implementation.

   23.a   Ramification:  The visibility rules prevent the name of a component
        of the type from appearing in a record_representation_clause at any
        place except for the component_local_name of a component_clause.
        However, since the record_representation_clause is part of the
        declarative region of the type declaration, the component names hide
        outer homographs throughout.

   23.b   A record_representation_clause cannot be given for a protected
        type, even though protected types, like record types, have
        components.  The primary reason for this rule is that there is likely
        to be too much dope in a protected type -- entry queues, bit maps for
        barrier values, etc.  In order to control the representation of the
        user-defined components, simply declare a record type, give it a
        representation_clause, and give the protected type one component
        whose type is the record type.  Alternatively, if the protected
        object is protecting something like a device register, it makes more
        sense to keep the thing being protected outside the protected object
        (possibly with a pointer to it in the protected object), in order to
        keep implementation-defined components out of the way.


                                  Examples

24   Example of specifying the layout of a record type:

25  Word : constant := 4;  --  storage element is byte, 4 bytes per word

26  type State         is (A,M,W,P);
    type Mode          is (Fix, Dec, Exp, Signif);

27  type Byte_Mask     is array (0..7)  of Boolean;
    type State_Mask    is array (State) of Boolean;
    type Mode_Mask     is array (Mode)  of Boolean;

28  type Program_Status_Word is
      record
          System_Mask        : Byte_Mask;
          Protection_Key     : Integer range 0 .. 3;
          Machine_State      : State_Mask;
          Interrupt_Cause    : Interruption_Code;
          Ilc                : Integer range 0 .. 3;
          Cc                 : Integer range 0 .. 3;
          Program_Mask       : Mode_Mask;
          Inst_Address       : Address;
    end record;

29  for Program_Status_Word use
      record
          System_Mask      at 0*Word range 0  .. 7;
          Protection_Key   at 0*Word range 10 .. 11; -- bits 8,9 unused
          Machine_State    at 0*Word range 12 .. 15;
          Interrupt_Cause  at 0*Word range 16 .. 31;
          Ilc              at 1*Word range 0  .. 1;  -- second word
          Cc               at 1*Word range 2  .. 3;
          Program_Mask     at 1*Word range 4  .. 7;
          Inst_Address     at 1*Word range 8  .. 31;
      end record;

30  for Program_Status_Word'Size use 8*System.Storage_Unit;
    for Program_Status_Word'Alignment use 8;


     NOTES
31   (13) Note on the example:  The record_representation_clause defines the
     record layout.  The Size clause guarantees that (at least) eight storage
     elements are used for objects of the type.  The Alignment clause
     guarantees that aliased, imported, or exported objects of the type will
     have addresses divisible by eight.


                         Wording Changes From Ada 83

        31.a   The alignment_clause has been renamed to mod_clause and moved
        to Annex J, ``Obsolescent Features''.

        31.b   We have clarified that implementation-defined component names
        have to be in the form of an attribute_reference of a component or of
        the first subtype itself; surely Ada 83 did not intend to allow
        arbitrary identifiers.

        31.c   The RM83-13.4(7) wording incorrectly allows components in
        non-variant records to overlap.  We have corrected that oversight.



13.5.2 Storage Place Attributes

                              Static Semantics

1   {storage place attributes (of a component)} For a component C of a
composite, non-array object R, the storage place attributes are defined:
{94-4493.c}
        1.a   Ramification:  The storage place attributes are not
        (individually) specifiable, but the user may control their values by
        giving a record_representation_clause.

2   R.C'Position
                Denotes the same value as R.C'Address - R'Address.  The value
                of this attribute is of the type universal_integer.

2.a     Ramification:  Thus, R.C'Position is the offset of C in storage
        elements from the beginning of the object, where the first storage
        element of an object is numbered zero.  R'Address + R.C'Position =
        R.C'Address.  For record extensions, the offset is not measured from
        the beginning of the extension part, but from the beginning of the
        whole object, as usual.

2.b     In ``R.C'Address - R'Address'', the "-" operator is the one in
        System.Storage_Elements that takes two Addresses and returns a
        Storage_Offset.

3   R.C'First_Bit
                Denotes the offset, from the start of the first of the
                storage elements occupied by C, of the first bit occupied by
                C. This offset is measured in bits.  The first bit of a
                storage element is numbered zero.  The value of this
                attribute is of the type universal_integer.

4   R.C'Last_Bit
                Denotes the offset, from the start of the first of the
                storage elements occupied by C, of the last bit occupied by
                C. This offset is measured in bits. The value of this
                attribute is of the type universal_integer.

        4.a   Ramification:  The ordering of bits in a storage element is is
        defined in 13.5.3, ``Bit Ordering''.

        4.b   R.C'Size = R.C'Last_Bit - R.C'First_Bit + 1.  (Unless the
        implementation chooses an indirection representation.)

        4.c   If a component_clause applies to a component, then that
        component will be at the same relative storage place in all objects
        of the type.  Otherwise, there is no such requirement.


                            Implementation Advice

5   {contiguous representation [partial]} {discontiguous representation
[partial]} If a component is represented using some form of pointer (such as
an offset) to the actual data of the component, and this data is contiguous
with the rest of the object, then the storage place attributes should reflect
the place of the actual data, not the pointer.  If a component is allocated
discontiguously from the rest of the object, then a warning should be
generated upon reference to one of its storage place attributes.

        5.a   Reason:  For discontiguous components, these attributes make no
        sense.  For example, an implementation might allocate dynamic-sized
        components on the heap.  For another example, an implementation might
        allocate the discriminants separately from the other components, so
        that multiple objects of the same subtype can share discriminants.
        Such representations cannot happen if there is a component_clause for
        that component.



13.5.3 Bit Ordering

1   [The Bit_Order attribute specifies the interpretation of the storage
place attributes.]

        1.a   Reason:  The intention is to provide uniformity in the
        interpretation of storage places across implementations on a
        particular machine by allowing the user to specify the Bit_Order.  It
        is not intended to fully support data interoperability across
        different machines, although it can be used for that purpose in some
        situations.

        1.b   We can't require all implementations on a given machine to use
        the same bit ordering by default; if the user cares, a pragma Bit_
        Order can be used to force all implementations to use the same bit
        ordering.


                              Static Semantics

2   {bit ordering} A bit ordering is a method of interpreting the meaning of
the storage place attributes.  {High_Order_First} {big endian} {endian (big)}
High_Order_First [(known in the vernacular as ``big endian'')] means that the
first bit of a storage element (bit 0) is the most significant bit
(interpreting the sequence of bits that represent a component as an unsigned
integer value).  {Low_Order_First} {little endian} {endian (little)} Low_
Order_First [(known in the vernacular as ``little endian'')] means the
opposite: the first bit is the least significant.

3   For every specific record subtype S, the following attribute is defined:

4   S'Bit_Order
                Denotes the bit ordering for the type of S. The value of this
                attribute is of type System.Bit_Order.  {specifiable [of Bit_
                Order for record types and record extensions]} {Bit_Order
                clause} Bit_Order may be specified for specific record types
                via an attribute_definition_clause; the expression of such a
                clause shall be static.

5   If Word_Size = Storage_Unit, the default bit ordering is implementation
defined.  If Word_Size > Storage_Unit, the default bit ordering is the same
as the ordering of storage elements in a word, when interpreted as an
integer.  {byte sex: see ordering of storage elements in a word}

        5.a   Implementation defined:  If Word_Size = Storage_Unit, the
        default bit ordering.

        5.b   Ramification:  Consider machines whose Word_Size = 32, and
        whose Storage_Unit = 8.  Assume the default bit ordering applies.  On
        a machine with big-endian addresses, the most significant storage
        element of an integer is at the address of the integer.  Therefore,
        bit zero of a storage element is the most significant bit.  On a
        machine with little-endian addresses, the least significant storage
        element of an integer is at the address of the integer.  Therefore,
        bit zero of a storage element is the least significant bit.

6   The storage place attributes of a component of a type are interpreted
according to the bit ordering of the type.

        6.a   Ramification:  This implies that the interpretation of the
        position, first_bit, and last_bit of a component_clause of a record_
        representation_clause obey the bit ordering given in a representation
        item.


                            Implementation Advice

7   {recommended level of support [bit ordering]} The recommended level of
support for the nondefault bit ordering is:

    8  If Word_Size = Storage_Unit, then the implementation should
       support the nondefault bit ordering in addition to the default
       bit ordering.

        8.a   Ramification:  If Word_Size = Storage_Unit, the implementation
        should support both bit orderings.  We don't push for support of the
        nondefault bit ordering when Word_Size > Storage_Unit (except of
        course for upward compatibility with a preexisting implementation
        whose Ada 83 bit order did not correspond to the required Ada 9X
        default bit order), because implementations are required to support
        storage positions that cross storage element boundaries when Word_
        Size > Storage_Unit.  Such storage positions will be split into two
        or three pieces if the nondefault bit ordering is used, which could
        be onerous to support.  However, if Word_Size = Storage_Unit, there
        might not be a natural bit ordering, but the splitting problem need
        not occur.


                            Extensions to Ada 83

        8.b   {extensions to Ada 83} The Bit_Order attribute is new to Ada
        9X.



13.6 Change of Representation

1   [{change of representation} {representation (change of)} A type_
conversion (see 4.6) can be used to convert between two different
representations of the same array or record.  To convert an array from one
representation to another, two array types need to be declared with matching
component subtypes, and convertible index types.  If one type has packing
specified and the other does not, then explicit conversion can be used to
pack or unpack an array.

2   To convert a record from one representation to another, two record types
with a common ancestor type need to be declared, with no inherited
subprograms.  Distinct representations can then be specified for the record
types, and explicit conversion between the types can be used to effect a
change in representation.]

        2.a   Ramification:  This technique does not work if the first type
        is an untagged type with user-defined primitive subprograms.  It does
        not work at all for tagged types.


                                  Examples

3   Example of change of representation:

4   -- Packed_Descriptor and Descriptor are two different types
    -- with identical characteristics, apart from their
    -- representation

5   type Descriptor is
        record
          -- components of a descriptor
        end record;

6   type Packed_Descriptor is new Descriptor;

7   for Packed_Descriptor use
        record
          -- component clauses for some or for all components
        end record;

8   -- Change of representation can now be accomplished by explicit type conver\
sions:
9   D : Descriptor;
    P : Packed_Descriptor;

10  P := Packed_Descriptor(D);  -- pack D
    D := Descriptor(P);         -- unpack P



13.7 The Package System

1   [For each implementation there is a library package called System which
includes the definitions of certain configuration-dependent characteristics.]


                              Static Semantics

2   The following language-defined library package exists:

        2.a   Implementation defined:  The contents of the visible part of
        package System and its language-defined children.

3   package System is
       pragma Preelaborate(System);

4      type Name is implementation-defined-enumeration-type;
       System_Name : constant Name := implementation-defined;

5      -- System-Dependent Named Numbers:

6      Min_Int               : constant := root_integer'First;
       Max_Int               : constant := root_integer'Last;
    {Min_Int (named number in package System)} {Max_Int (named number in packag\
e System)}

7      Max_Binary_Modulus    : constant := implementation-defined;
       Max_Nonbinary_Modulus : constant := implementation-defined;
    {Max_Binary_Modulus (named number in package System)} {Max_Nonbinary_Modulu\
s (named number in package System)}

8      Max_Base_Digits       : constant := root_real'Digits;
       Max_Digits            : constant := implementation-defined;
    {Max_Base_Digits (named number in package System)} {Max_Digits (named numbe\
r in package System)}

9      Max_Mantissa          : constant := implementation-defined;
       Fine_Delta            : constant := implementation-defined;
    {Max_Mantissa (named number in package System)} {Fine_Delta (named number i\
n package System)}

10     Tick                  : constant := implementation-defined;
    {Tick (named number in package System)}

11     -- Storage-related Declarations:

12     type Address is implementation-defined;
       Null_Address : constant Address;
    {address (null)} {Null_Address (constant in System)}

13     Storage_Unit : constant := implementation-defined;
       Word_Size    : constant := implementation-defined * Storage_Unit;
       Memory_Size  : constant := implementation-defined;
    {Storage_Unit (named number in package System)} {Word_Size (named number in\
 package System)}

14     -- {address (comparison)} Address Comparison:
       function "<" (Left, Right : Address) return Boolean;
       function "<="(Left, Right : Address) return Boolean;
       function ">" (Left, Right : Address) return Boolean;
       function ">="(Left, Right : Address) return Boolean;
       function "=" (Left, Right : Address) return Boolean;
    -- function "/=" (Left, Right : Address) return Boolean;
       -- "/=" is implicitly defined
       pragma Convention(Intrinsic, "<");
       ... -- and so on for all language-defined subprograms in this package

15     -- Other System-Dependent Declarations:
       type Bit_Order is (High_Order_First, Low_Order_First);
       Default_Bit_Order : constant Bit_Order;

16     -- Priority-related declarations (see D.1):
       subtype Any_Priority is Integer range implementation-defined;
       subtype Priority is Any_Priority range Any_Priority'First .. implementat\
ion-defined;
       subtype Interrupt_Priority is Any_Priority range Priority'Last+1 .. Any_\
Priority'Last;

17     Default_Priority : constant Priority := (Priority'First + Priority'Last)\
/2;

18  private
       ... -- not specified by the language
    end System;

19   Name is an enumeration subtype.  Values of type Name are the names of
alternative machine configurations handled by the implementation.  System_
Name represents the current machine configuration.

20   The named numbers Fine_Delta and Tick are of the type universal_real;
the others are of the type universal_integer.

21   The meanings of the named numbers are:

22  [Min_Int
                The smallest (most negative) value allowed for the
                expressions of a signed_integer_type_definition.

23  Max_Int
                The largest (most positive) value allowed for the expressions
                of a signed_integer_type_definition.

24  Max_Binary_Modulus
                A power of two such that it, and all lesser positive powers
                of two, are allowed as the modulus of a modular_type_
                definition.

25  Max_Nonbinary_Modulus
                A value such that it, and all lesser positive integers, are
                allowed as the modulus of a modular_type_definition.

25.a    Ramification:  There is no requirement that Max_Nonbinary_Modulus be
        less than or equal to Max_Binary_Modulus, although that's what makes
        most sense.  On a typical 32-bit machine, for example, Max_Binary_
        Modulus will be 2**32 and Max_Nonbinary_Modulus will be 2**31,
        because supporting nonbinary moduli in above 2**31 causes
        implementation difficulties.

26  Max_Base_Digits
                The largest value allowed for the requested decimal precision
                in a floating_point_definition.

27  Max_Digits
                The largest value allowed for the requested decimal precision
                in a floating_point_definition that has no real_range_
                specification.  Max_Digits is less than or equal to Max_Base_
                Digits.

28  Max_Mantissa
                The largest possible number of binary digits in the mantissa
                of machine numbers of a user-defined ordinary fixed point
                type.  (The mantissa is defined in Annex G.)

29  Fine_Delta
                The smallest delta allowed in an ordinary_fixed_point_
                definition that has the real_range_specification range -1.0
                .. 1.0.  ]

30  Tick
                A period in seconds approximating the real time interval
                during which the value of Calendar.Clock remains constant.

30.a    Ramification:  There is no required relationship between System.Tick
        and Duration'Small, other than the one described here.

30.b    The inaccuracy of the delay_statement has no relation to Tick.  In
        particular, it is possible that the clock used for the delay_
        statement is less accurate than Calendar.Clock.

30.c    We considered making Tick a run-time-determined quantity, to allow
        for easier configurability.  However, this would not be upward
        compatible, and the desired configurability can be achieved using
        functionality defined in Annex D, ``Real-Time Systems''.

31  Storage_Unit
                The number of bits per storage element.

32  Word_Size
                The number of bits per word.

33  Memory_Size
                An implementation-defined value [that is intended to reflect
                the memory size of the configuration in storage elements.]

33.a    Discussion:  It is unspecified whether this refers to the size of the
        address space, the amount of physical memory on the machine, or
        perhaps some other interpretation of ``memory size.''  In any case,
        the value has to be given by a static expression, even though the
        amount of memory on many modern machines is a dynamic quantity in
        several ways.  Thus, Memory_Size is not very useful.

34   Address is of a definite, nonlimited type.  Address represents machine
addresses capable of addressing individual storage elements.  Null_Address is
an address that is distinct from the address of any object or program unit.
{pointer: see type System.Address}

        34.a   Ramification:  The implementation has to ensure that there is
        at least one address that nothing will be allocated to; Null_Address
        will be one such address.

        34.b   Ramification:  Address is the type of the result of the
        attribute Address.

        34.c   Reason:  Address is required to be nonlimited and definite
        because it is important to be able to assign addresses, and to
        declare uninitialized address variables.

35   See 13.5.3 for an explanation of Bit_Order and Default_Bit_Order.


                         Implementation Permissions

36   An implementation may add additional implementation-defined declarations
to package System and its children.  [However, it is usually better for the
implementation to provide additional functionality via implementation-defined
children of System.]  Package System may be declared pure.  {94-4776.g}

        36.a   Ramification:  The declarations in package System and its
        children can be implicit.  For example, since Address is not limited,
        the predefined "=" and "/=" operations are probably sufficient.
        However, the implementation is not required to use the predefined
        "=".


                            Implementation Advice

37   Address should be of a private type.

        37.a   Reason:  This promotes uniformity by avoiding having
        implementation-defined predefined operations for the type.  We don't
        require it, because implementations may want to stick with what they
        have.

        37.b   Implementation Note:  It is not necessary for Address to be
        able to point at individual bits within a storage element.  Nor is it
        necessary for it to be able to point at machine registers.  It is
        intended as a memory address that matches the hardware's notion of an
        address.

        37.c   The representation of the null value of a general access type
        should be the same as that of Null_Address; instantiations of
        Unchecked_Conversion should work accordingly.  If the implementation
        supports interfaces to other languages, the representation of the
        null value of a general access type should be the same as in those
        other languages, if appropriate.

        37.d   Note that the children of the Interfaces package will
        generally provide foreign-language-specific null values where
        appropriate.  See UI-0065 regarding Null_Address.


     NOTES
38   (14) There are also some language-defined child packages of System
     defined elsewhere.


                         Wording Changes From Ada 83

        38.a   Much of the content of System is standardized, to provide more
        uniformity across implementations.  Implementations can still add
        their own declarations to System, but are encouraged to do so via
        children of System.

        38.b   Some of the named numbers are defined more explicitly in terms
        of the standard numeric types.

        38.c   The pragmas System_Name, Storage_Unit, and Memory_Size are no
        longer defined by the language.  However, the corresponding
        declarations in package System still exist.  Existing implementations
        may continue to support the three pragmas as implementation-defined
        pragmas, if they so desire.

        38.d   Priority semantics, including subtype Priority, have been
        moved to the Real Time Annex.



13.7.1 The Package System.Storage_Elements

                              Static Semantics

1   The following language-defined library package exists:

2   package System.Storage_Elements is
       pragma Preelaborate(System.Storage_Elements);

3      type Storage_Offset is range implementation-defined;
    {Storage_Count (subtype in package System.Storage_Elements)}

4      subtype Storage_Count is Storage_Offset range 0..Storage_Offset'Last;

5      type Storage_Element is mod implementation-defined;
       for Storage_Element'Size use Storage_Unit;
       type Storage_Array is array
         (Storage_Offset range <>) of aliased Storage_Element;
       for Storage_Array'Component_Size use Storage_Unit;

6      -- {address (arithmetic)} Address Arithmetic:

7      function "+"(Left : Address; Right : Storage_Offset)
         return Address;
       function "+"(Left : Storage_Offset; Right : Address)
         return Address;
       function "-"(Left : Address; Right : Storage_Offset)
         return Address;
       function "-"(Left, Right : Address)
         return Storage_Offset;

8      function "mod"(Left : Address; Right : Storage_Offset)
         return Storage_Offset;

9      -- Conversion to/from integers:

10     type Integer_Address is implementation-defined;
       function To_Address(Value : Integer_Address) return Address;
       function To_Integer(Value : Address) return Integer_Address;

11     pragma Convention(Intrinsic, "+");
          -- ...and so on for all language-defined subprograms declared in this\
 package.
    end System.Storage_Elements;

        11.a   Reason:  The Convention pragmas imply that the attribute
        Access is not allowed for those operations.

        11.b   The mod function is needed so that the definition of Alignment
        makes sense.

12   Storage_Element represents a storage element.  Storage_Offset represents
an offset in storage elements.  Storage_Count represents a number of storage
elements.  {contiguous representation [partial]} {discontiguous
representation [partial]} Storage_Array represents a contiguous sequence of
storage elements.

        12.a   Reason:  The index subtype of Storage_Array is Storage_Offset
        because we wish to allow maximum flexibility.  Most Storage_Arrays
        will probably have a lower bound of 0 or 1, but other lower bounds,
        including negative ones, make sense in some situations.

        12.b   Note that there are some language-defined subprograms that
        fill part of a Storage_Array, and return the index of the last
        element filled as a Storage_Offset.  The Read procedures in Streams
        (see 13.13.1), Streams.Stream_IO (see A.12.1), and System.RPC (see
        E.5) behave in this manner.  These will raise Constraint_Error if the
        resulting Last value is not in Storage_Offset.  This implies that the
        Storage_Array passed to these subprograms should not have a lower
        bound of Storage_Offset'First, because then a read of 0 elements
        would always raise Constraint_Error.  A better choice of lower bound
        is 1.

13   Integer_Address is a [(signed or modular)] integer subtype.  {94-4445.a}
To_Address and To_Integer convert back and forth between this type and
Address.


                         Implementation Requirements

14   Storage_Offset'Last shall be greater than or equal to Integer'Last or
the largest possible storage offset, whichever is smaller.  Storage_
Offset'First shall be <= (-Storage_Offset'Last).


                         Implementation Permissions

15   Package System.Storage_Elements may be declared pure.  {94-4921.a}


                            Implementation Advice

16   Operations in System and its children should reflect the target
environment semantics as closely as is reasonable.  For example, on most
machines, it makes sense for address arithmetic to ``wrap around.''
{Program_Error (raised by failure of run-time check)} Operations that do not
make sense should raise Program_Error.

        16.a   Discussion:  For example, on a segmented architecture, X < Y
        might raise Program_Error if X and Y do not point at the same segment
        (assuming segments are unordered).  Similarly, on a segmented
        architecture, the conversions between Integer_Address and Address
        might not make sense for some values, and so might raise Program_
        Error.

        16.b   Reason:  We considered making Storage_Element a private type.
        However, it is better to declare it as a modular type in the visible
        part, since code that uses it is already low level, and might as well
        have access to the underlying representation.  We also considered
        allowing Storage_Element to be any integer type, signed integer or
        modular, but it is better to have uniformity across implementations
        in this regard, and viewing storage elements as unsigned seemed to
        make the most sense.

        16.c   Implementation Note:  To_Address is intended for use in
        Address clauses.  Implementations should overload To_Address if
        appropriate.  For example, on a segmented architecture, it might make
        sense to have a record type representing a segment/offset pair, and
        have a To_Address conversion that converts from that record type to
        type Address.



13.7.2 The Package System.Address_To_Access_Conversions

                              Static Semantics

1   The following language-defined generic library package exists:

2   generic
        type Object(<>) is limited private;
    package System.Address_To_Access_Conversions is
       pragma Preelaborate(Address_To_Access_Conversions);

3      type Object_Pointer is access all Object;
       function To_Pointer(Value : Address) return Object_Pointer;
       function To_Address(Value : Object_Pointer) return Address;

4      pragma Convention(Intrinsic, To_Pointer);
       pragma Convention(Intrinsic, To_Address);
    end System.Address_To_Access_Conversions;

5   The To_Pointer and To_Address subprograms convert back and forth between
values of types Object_Pointer and Address.  To_Pointer(X'Address) is equal
to X'Unchecked_Access for any X that allows Unchecked_Access.  To_
Pointer(Null_Address) returns null.  {unspecified [partial]} For other
addresses, the behavior is unspecified.  To_Address(null) returns Null_
Address (for null of the appropriate type).  To_Address(Y), where Y /= null,
returns Y.all'Address.

        5.a   Discussion:  The programmer should ensure that the address
        passed to To_Pointer is either Null_Address, or the address of an
        object of type Object.  Otherwise, the behavior of the program is
        unspecified; it might raise an exception or crash, for example.

        5.b   Reason:  Unspecified is almost the same thing as erroneous;
        they both allow arbitrarily bad behavior.  We don't say erroneous
        here, because the implementation might allow the address passed to
        To_Pointer to point at some memory that just happens to ``look like''
        an object of type Object.  That's not necessarily an error; it's just
        not portable.  However, if the actual type passed to Object is (for
        example) an array type, the programmer would need to be aware of any
        dope that the implementation expects to exist, when passing an
        address that did not come from the Address attribute of an object of
        type Object.

        5.c   One might wonder why To_Pointer and To_Address are any better
        than unchecked conversions.  The answer is that Address does not
        necessarily have the same representation as an access type.  For
        example, an access value might point at the bounds of an array when
        an address would point at the first element.  Or an access value
        might be an offset in words from someplace, whereas an address might
        be an offset in bytes from the beginning of memory.


                         Implementation Permissions

6   An implementation may place restrictions on instantiations of Address_To_
Access_Conversions.

        6.a   Ramification:  For example, if the hardware requires aligned
        loads and stores, then dereferencing an access value that is not
        properly aligned might raise an exception.

        6.b   For another example, if the implementation has chosen to use
        negative component offsets (from an access value), it might not be
        possible to preserve the semantics, since negative offsets from the
        Address are not allowed.  (The Address attribute always points at
        ``the first of the storage elements....'')  Note that while the
        implementation knows how to convert an access value into an address,
        it might not be able to do the reverse.  To avoid generic contract
        model violations, the restriction might have to be detected at run
        time in some cases.


{94-4921.a}



13.8 Machine Code Insertions

1   [{machine code insertion} A machine code insertion can be achieved by a
call to a subprogram whose sequence_of_statements contains code_statements.]


                                   Syntax

2   code_statement ::= qualified_expression;

    3   A code_statement is only allowed in the handled_sequence_of_
    statements of a subprogram_body.  If a subprogram_body contains any code_
    statements, then within this subprogram_body the only allowed form of
    statement is a code_statement (labeled or not), the only allowed
    declarative_items are use_clauses, and no exception_handler is allowed
    (comments and pragmas are allowed as usual).


                            Name Resolution Rules

4   {expected type [code_statement]} The qualified_expression is expected to
be of any type.


                               Legality Rules

5   The qualified_expression shall be of a type declared in package
System.Machine_Code.

        5.a   Ramification:  This includes types declared in children of
        System.Machine_Code.

6   A code_statement shall appear only within the scope of a with_clause that
mentions package System.Machine_Code.

        6.a   Ramification:  Note that this is not a note; without this rule,
        it would be possible to write machine code in compilation units which
        depend on System.Machine_Code only indirectly.


                              Static Semantics

7   {System.Machine_Code} The contents of the library package System.Machine_
Code (if provided) are implementation defined.  The meaning of code_
statements is implementation defined.  [Typically, each qualified_expression
represents a machine instruction or assembly directive.]

        7.a   Discussion:  For example, an instruction might be a record with
        an Op_Code component and other components for the operands.

        7.b   Implementation defined:  The contents of the visible part of
        package System.Machine_Code, and the meaning of code_statements.


                         Implementation Permissions

8   An implementation may place restrictions on code_statements.  An
implementation is not required to provide package System.Machine_Code.


     NOTES
9    (15) An implementation may provide implementation-defined pragmas
     specifying register conventions and calling conventions.

10   (16) Machine code functions are exempt from the rule that a return_
     statement is required.  In fact, return_statements are forbidden, since
     only code_statements are allowed.

   10.a   Discussion:  The idea is that the author of a machine code
        subprogram knows the calling conventions, and refers to parameters
        and results accordingly.  The implementation should document where to
        put the result of a machine code function, for example, ``Scalar
        results are returned in register 0.''

11   (17) Intrinsic subprograms (see 6.3.1, ``Conformance Rules'') can also
     be used to achieve machine code insertions.  Interface to assembly
     language can be achieved using the features in Annex B, ``Interface to
     Other Languages''.


                                  Examples

12   Example of a code statement:

13  M : Mask;
    procedure Set_Mask; pragma Inline(Set_Mask);

14  procedure Set_Mask is
      use System.Machine_Code; -- assume ``with System.Machine_Code;'' appears \
somewhere above
    begin
      SI_Format'(Code => SSM, B => M'Base_Reg, D => M'Disp);
      --  Base_Reg and Disp are implementation-defined attributes
    end Set_Mask;


                            Extensions to Ada 83

        14.a   {extensions to Ada 83} Machine code functions are allowed in
        Ada 9X; in Ada 83, only procedures were allowed.

                         Wording Changes From Ada 83

        14.b   The syntax for code_statement is changed to say ``qualified_
        expression'' instead of ``subtype_mark'record_aggregate''.  Requiring
        the type of each instruction to be a record type is
        overspecification.



13.9 Unchecked Type Conversions

1   [{unchecked type conversion} {type conversion (unchecked)} {conversion
(unchecked)} {type_conversion: see also unchecked type conversion} {cast: see
unchecked type conversion} An unchecked type conversion can be achieved by a
call to an instance of the generic function Unchecked_Conversion.]


                              Static Semantics

2   The following language-defined generic library function exists:

3   generic
       type Source(<>) is limited private;
       type Target(<>) is limited private;
    function Ada.Unchecked_Conversion(S : Source) return Target;
    pragma Convention(Intrinsic, Ada.Unchecked_Conversion);
    pragma Pure(Ada.Unchecked_Conversion);

{94-4528.a}

        3.a   Reason:  The pragma Convention implies that the attribute
        Access is not allowed for instances of Unchecked_Conversion.


                              Dynamic Semantics

4   The size of the formal parameter S in an instance of Unchecked_Conversion
is that of its subtype.  [This is the actual subtype passed to Source, except
when the actual is an unconstrained composite subtype, in which case the
subtype is constrained by the bounds or discriminants of the value of the
actual expression passed to S.]

5   If all of the following are true, the effect of an unchecked conversion
is to return the value of an object of the target subtype whose
representation is the same as that of the source object S:
    6  S'Size = Target'Size.

 6.a    Ramification:  Note that there is no requirement that the Sizes
        be known at compile time.

    7  S'Alignment = Target'Alignment.

    8  The target subtype is not an unconstrained composite subtype.

    9  {contiguous representation [partial]} {discontiguous
       representation [partial]} S and the target subtype both have a
       contiguous representation.

   10  The representation of S is a representation of an object of the
       target subtype.

11   Otherwise, the effect is implementation defined; in particular, the
result can be abnormal (see 13.9.1).

        11.a   Implementation defined:  The effect of unchecked conversion.

        11.b   Ramification:  Whenever unchecked conversions are used, it is
        the programmer's responsibility to ensure that these conversions
        maintain the properties that are guaranteed by the language for
        objects of the target type.  This requires the user to understand the
        underlying run-time model of the implementation.  The execution of a
        program that violates these properties by means of unchecked
        conversions is erroneous.

        11.c   An instance of Unchecked_Conversion can be applied to an
        object of a private type, assuming the implementation allows it.


                         Implementation Permissions

12   An implementation may return the result of an unchecked conversion by
reference, if the Source type is not a by-copy type.  [In this case, the
result of the unchecked conversion represents simply a different (read-only)
view of the operand of the conversion.]

        12.a   Ramification:  In other words, the result object of a call on
        an instance of Unchecked_Conversion can occupy the same storage as
        the formal parameter S.

13   An implementation may place restrictions on Unchecked_Conversion.

        13.a   Ramification:  For example, an instantiation of Unchecked_
        Conversion for types for which unchecked conversion doesn't make
        sense may be disallowed.


                            Implementation Advice

14   The Size of an array object should not include its bounds; hence, the
bounds should not be part of the converted data.

        14.a   Ramification:  On the other hand, we have no advice to offer
        about discriminants and tag fields.

15   The implementation should not generate unnecessary run-time checks to
ensure that the representation of S is a representation of the target type.
It should take advantage of the permission to return by reference when
possible.  Restrictions on unchecked conversions should be avoided unless
required by the target environment.  {94-4954.a} {94-4966.a}

        15.a   Implementation Note:  As an example of an unnecessary run-time
        check, consider a record type with gaps between components.  The
        compiler might assume that such gaps are always zero bits.  If a
        value is produced that does not obey that assumption, then the
        program might misbehave.  The implementation should not generate
        extra code to check for zero bits (except, perhaps, in a special
        error-checking mode).

16   {recommended level of support [unchecked conversion]} The recommended
level of support for unchecked conversions is:

   17  Unchecked conversions should be supported and should be
       reversible in the cases where this clause defines the result.
       {contiguous representation [partial]} {discontiguous
       representation [partial]} To enable meaningful use of unchecked
       conversion, a contiguous representation should be used for
       elementary subtypes, for statically constrained array subtypes
       whose component subtype is one of the subtypes described in this
       paragraph, and for record subtypes without discriminants whose
       component subtypes are described in this paragraph.



13.9.1 Data Validity

1   Certain actions that can potentially lead to erroneous execution are not
directly erroneous, but instead can cause objects to become abnormal.
Subsequent uses of abnormal objects can be erroneous.

2   A scalar object can have an invalid representation, which means that the
object's representation does not represent any value of the object's subtype.
{uninitialized variables [distributed]} The primary cause of invalid
representations is uninitialized variables.

3   Abnormal objects and invalid representations are explained in this
subclause.


                              Dynamic Semantics

4   {normal state of an object [distributed]} {abnormal state of an object
[distributed]} When an object is first created, and any explicit or default
initializations have been performed, the object and all of its parts are in
the normal state.  Subsequent operations generally leave them normal.
However, an object or part of an object can become abnormal in the following
ways:

    5  {disruption of an assignment} An assignment to the object is
       disrupted due to an abort (see 9.8) or due to the failure of a
       language-defined check (see 11.6).

    6  The object is not scalar, and is passed to an in out or out
       parameter of an imported procedure or language-defined input
       procedure, if after return from the procedure the representation
       of the parameter does not represent a value of the parameter's
       subtype.

7   {unspecified [partial]} Whether or not an object actually becomes
abnormal in these cases is not specified.  An abnormal object becomes normal
again upon successful completion of an assignment to the object as a whole.


                             Erroneous Execution

8   {erroneous execution} It is erroneous to evaluate a primary that is a
name denoting an abnormal object, or to evaluate a prefix that denotes an
abnormal object.

        8.a   Ramification:  Although a composite object with no
        subcomponents of an access type, and with static constraints all the
        way down cannot become abnormal, a scalar subcomponent of such an
        object can become abnormal.

        8.b   The in out or out parameter case does not apply to scalars; bad
        scalars are merely invalid representations, rather than abnormal, in
        this case.

        8.c   Reason:  The reason we allow access objects, and objects
        containing subcomponents of an access type, to become abnormal is
        because the correctness of an access value cannot necessarily be
        determined merely by looking at the bits of the object.  The reason
        we allow scalar objects to become abnormal is that we wish to allow
        the compiler to optimize assuming that the value of a scalar object
        belongs to the object's subtype, if the compiler can prove that the
        object is initialized with a value that belongs to the subtype.  The
        reason we allow composite objects to become abnormal if some
        constraints are nonstatic is that such object might be represented
        with implicit levels of indirection; if those are corrupted, then
        even assigning into a component of the object, or simply asking for
        its Address, might have an unpredictable effect.  The same is true if
        the discriminants have been destroyed.


                          Bounded (Run-Time) Errors

9   {bounded error} {invalid representation} If the representation of a
scalar object does not represent a value of the object's subtype (perhaps
because the object was not initialized), the object is said to have an
invalid representation.  It is a bounded error to evaluate the value of such
an object.  {94-4796.a} {Program_Error (raised by failure of run-time check)}
{Constraint_Error (raised by failure of run-time check)} If the error is
detected, either Constraint_Error or Program_Error is raised.  Otherwise,
execution continues using the invalid representation.  The rules of the
language outside this subclause assume that all objects have valid
representations.  {94-4768.e} {94-4843.b} The semantics of operations on
invalid representations are as follows:

        9.a   Discussion:  The AARM is more explicit about what happens when
        the value of the case expression is an invalid representation.

   10  If the representation of the object represents a value of the
       object's type, the value of the type is used.

   11  If the representation of the object does not represent a value of
       the object's type, the semantics of operations on such
       representations is implementation-defined, but does not by itself
       lead to erroneous or unpredictable execution, or to other objects
       becoming abnormal.


                             Erroneous Execution

12   {erroneous execution} A call to an imported function or an instance of
Unchecked_Conversion is erroneous if the result is scalar, and the result
object has an invalid representation.

        12.a   Ramification:  In a typical implementation, every bit pattern
        that fits in an object of an integer subtype will represent a value
        of the type, if not of the subtype.  However, for an enumeration or
        floating point type, there are typically bit patterns that do not
        represent any value of the type.  In such cases, the implementation
        ought to define the semantics of operations on the invalid
        representations in the obvious manner (assuming the bounded error is
        not detected):  a given representation should be equal to itself, a
        representation that is in between the internal codes of two
        enumeration literals should behave accordingly when passed to
        comparison operators and membership tests, etc.  We considered
        requiring such sensible behavior, but it resulted in too much arcane
        verbiage, and since implementations have little incentive to behave
        irrationally, such verbiage is not important to have.

        12.b   If a stand-alone scalar object is initialized to a an in-range
        value, then the implementation can take advantage of the fact that
        any out-of-range value has to be abnormal.  Such an out-of-range
        value can be produced only by things like unchecked conversion,
        input, and disruption of an assignment due to abort or to failure of
        a language-defined check.  This depends on out-of-range values being
        checked before assignment (that is, checks are not optimized away
        unless they are proven redundant).

        12.c   Consider the following example:

12.d        type My_Int is range 0..99;
            function Safe_Convert is new Unchecked_Conversion(My_Int, Integer);
            function Unsafe_Convert is new Unchecked_Conversion(My_Int, Positiv\
e);
            X : Positive := Safe_Convert(0); -- Raises Constraint_Error.
            Y : Positive := Unsafe_Convert(0); -- Erroneous.

        12.e   The call to Unsafe_Convert causes erroneous execution.  The
        call to Safe_Convert is not erroneous.  The result object is an
        object of subtype Integer containing the value 0.  The assignment to
        X is required to do a constraint check; the fact that the conversion
        is unchecked does not obviate the need for subsequent checks required
        by the language rules.

        12.f   Implementation Note:  If an implementation wants to have a
        ``friendly'' mode, it might always assign an uninitialized scalar a
        default initial value that is outside the object's subtype (if there
        is one), and check for this value on some or all reads of the object,
        so as to help detect references to uninitialized scalars.
        Alternatively, an implementation might want to provide an ``unsafe''
        mode where it presumed even uninitialized scalars were always within
        their subtype.

        12.g   Ramification:  The above rules imply that it is a bounded
        error to apply a predefined operator to an object with a scalar
        subcomponent having an invalid representation, since this implies
        reading the value of each subcomponent.  Either Program_Error or
        Constraint_Error is raised, or some result is produced, which if
        composite, might have a corresponding scalar subcomponent still with
        an invalid representation.

        12.h   Note that it is not an error to assign, convert, or pass as a
        parameter a composite object with an uninitialized scalar
        subcomponent.  In the other hand, it is a (bounded) error to apply a
        predefined operator such as =, <, and xor to a composite operand with
        an invalid scalar subcomponent.

13   The dereference of an access value is erroneous if it does not designate
an object of an appropriate type or a subprogram with an appropriate profile,
if it designates a nonexistent object, or if it is an access-to-variable
value that designates a constant object.  [Such an access value can exist,
for example, because of Unchecked_Deallocation, Unchecked_Access, or
Unchecked_Conversion.]

        13.a   Ramification:  The above mentioned Unchecked_... features are
        not the only causes of such access values.  For example, interfacing
        to other languages can also cause the problem.

        13.b   One obscure example is if the Adjust subprogram of a
        controlled type uses Unchecked_Access to create an access-to-variable
        value designating a subcomponent of its controlled parameter, and
        saves this access value in a global object.  When Adjust is called
        during the initialization of a constant object of the type, the end
        result will be an access-to-variable value that designates a constant
        object.


     NOTES
14   (18) Objects can become abnormal due to other kinds of actions that
     directly update the object's representation; such actions are generally
     considered directly erroneous, however.


                         Wording Changes From Ada 83

        14.a   In order to reduce the amount of erroneousness, we separate
        the concept of an undefined value into objects with invalid
        representation (scalars only) and abnormal objects.

        14.b   Reading an object with an invalid representation is a bounded
        error rather than erroneous; reading an abnormal object is still
        erroneous.  In fact, the only safe thing to do to an abnormal object
        is to assign to the object as a whole.



13.9.2 The Valid Attribute

1   The Valid attribute can be used to check the validity of data produced by
unchecked conversion, input, interface to foreign languages, and the like.


                              Static Semantics

2   For a prefix X that denotes a scalar object [(after any implicit
dereference)], the following attribute is defined:

3   X'Valid
                Yields True if and only if the object denoted by X is normal
                and has a valid representation.  The value of this attribute
                is of the predefined type Boolean.

3.a     Ramification:  Having checked that X'Valid is True, it is safe to
        read the value of X without fear of erroneous execution caused by
        abnormality, or a bounded error caused by an invalid representation.
        Such a read will produce a value in the subtype of X.


     NOTES
4    (19) Invalid data can be created in the following cases (not counting
     erroneous or unpredictable execution):

         5  an uninitialized scalar object,

         6  the result of an unchecked conversion,

         7  input,

         8  interface to another language (including machine code),

         9  aborting an assignment,

        10  disrupting an assignment due to the failure of a
            language-defined check (see 11.6), and

        11  use of an object whose Address has been specified.

12   (20) X'Valid is not considered to be a read of X; hence, it is not an
     error to check the validity of invalid data.

   12.a   Ramification:  If X is of an enumeration type with a representation
        clause, then X'Valid checks that the value of X when viewed as an
        integer is one of the specified internal codes.

   12.b   Reason:  Valid is defined only for scalar objects because the
        implementation and description burden would be too high for other
        types.  For example, given a typical run-time model, it is impossible
        to check the validity of an access value.  The same applies to
        composite types implemented with internal pointers.  One can check
        the validity of a composite object by checking the validity of each
        of its scalar subcomponents.  The user should ensure that any
        composite types that need to be checked for validity are represented
        in a way that does not involve implementation-defined components, or
        gaps between components.  Furthermore, such types should not contain
        access subcomponents.

   12.c   Note that one can safely check the validity of a composite object
        with an abnormal value only if the constraints on the object and all
        of its subcomponents are static.  Otherwise, evaluation of the prefix
        of the attribute_reference causes erroneous execution (see 4.1).


                            Extensions to Ada 83

        12.d   {extensions to Ada 83} X'Valid is new in Ada 9X.



13.10 Unchecked Access Value Creation

1   [The attribute Unchecked_Access is used to create access values in an
unsafe manner -- the programmer is responsible for preventing ``dangling
references.'']


                              Static Semantics

2   The following attribute is defined for a prefix X that denotes an aliased
view of an object:

3   X'Unchecked_Access
                All rules and semantics that apply to X'Access (see 3.10.2)
                apply also to X'Unchecked_Access, except that, for the
                purposes of accessibility rules and checks, it is as if X
                were declared immediately within a library package.  {Access
                attribute: see also Unchecked_Access attribute}


     NOTES
4    (21) This attribute is provided to support the situation where a local
     object is to be inserted into a global linked data structure, when the
     programmer knows that it will always be removed from the data structure
     prior to exiting the object's scope.  The Access attribute would be
     illegal in this case (see 3.10.2, ``Operations of Access Types'').

   4.a   Ramification:  {expected type [Unchecked_Access attribute]} The
        expected type for X'Unchecked_Access is as for X'Access.

   4.b   If an attribute_reference with Unchecked_Access is used as the
        actual parameter for an access parameter, an Accessibility_Check can
        never fail on that access parameter.

5    (22) There is no Unchecked_Access attribute for subprograms.
   5.a   Reason:  Such an attribute would allow ``downward closures,'' where
        an access value designating a more nested subprogram is passed to a
        less nested subprogram.  This requires some means of reconstructing
        the global environment for the more nested subprogram, so that it can
        do up-level references to objects.  The two methods of implementing
        up-level references are displays and static links.  If downward
        closures were supported, each access-to-subprogram value would have
        to carry the static link or display with it.  In the case of
        displays, this was judged to be infeasible, and we don't want to
        disrupt implementations by forcing them to use static links if they
        already use displays.

   5.b   If desired, an instance of Unchecked_Conversion can be used to
        create an access value of a global access-to-subprogram type that
        designates a local subprogram.  The semantics of using such a value
        are not specified by the language.  In particular, it is not
        specified what happens if such subprograms make up-level references;
        even if the frame being referenced still exists, the up-level
        reference might go awry if the representation of a value of a global
        access-to-subprogram type doesn't include a static link.



13.11 Storage Management

1   [{user-defined storage management} {storage management (user-defined)}
{user-defined heap management} {heap management (user-defined)} Each
access-to-object type has an associated storage pool.  The storage allocated
by an allocator comes from the pool; instances of Unchecked_Deallocation
return storage to the pool.  Several access types can share the same pool.]

2   [A storage pool is a variable of a type in the class rooted at Root_
Storage_Pool, which is an abstract limited controlled type.  By default, the
implementation chooses a standard storage pool for each access type.  The
user may define new pool types, and may override the choice of pool for an
access type by specifying Storage_Pool for the type.]

        2.a   Ramification:  By default, the implementation might choose to
        have a single global storage pool, which is used (by default) by all
        access types, which might mean that storage is reclaimed
        automatically only upon partition completion.  Alternatively, it
        might choose to create a new pool at each accessibility level, which
        might mean that storage is reclaimed for an access type when leaving
        the appropriate scope.  Other schemes are possible.


                               Legality Rules

3   If Storage_Pool is specified for a given access type, Storage_Size shall
not be specified for it.

        3.a   Reason:  The Storage_Pool determines the Storage_Size; hence it
        would not make sense to specify both.  Note that this rule is
        simplified by the fact that the aspects in question cannot be
        specified for derived types, nor for non-first subtypes, so we don't
        have to worry about whether, say, Storage_Pool on a derived type
        overrides Storage_Size on the parent type.  For the same reason,
        ``specified'' means the same thing as ``directly specified'' here.


                              Static Semantics

4   The following language-defined library package exists:

5   with Ada.Finalization;
    with System.Storage_Elements;
    package System.Storage_Pools is
        pragma Preelaborate(System.Storage_Pools);

6       type Root_Storage_Pool is
            abstract new Ada.Finalization.Limited_Controlled with private;

7       procedure Allocate(
          Pool : in out Root_Storage_Pool;
          Storage_Address : out Address;
          Size_In_Storage_Elements : in Storage_Elements.Storage_Count;
          Alignment : in Storage_Elements.Storage_Count) is abstract;

8       procedure Deallocate(
          Pool : in out Root_Storage_Pool;
          Storage_Address : in Address;
          Size_In_Storage_Elements : in Storage_Elements.Storage_Count;
          Alignment : in Storage_Elements.Storage_Count) is abstract;

9       function Storage_Size(Pool : Root_Storage_Pool)
            return Storage_Elements.Storage_Count is abstract;

10  private
       ... -- not specified by the language
    end System.Storage_Pools;

        10.a   Reason:  The Alignment parameter is provided to Deallocate
        because some allocation strategies require it.  If it is not needed,
        it can be ignored.

11   {storage pool type} {pool type} A storage pool type (or pool type) is a
descendant of Root_Storage_Pool.  {storage pool element} {pool element}
{element (of a storage pool)} The elements of a storage pool are the objects
allocated in the pool by allocators.

        11.a   Discussion:  In most cases, an element corresponds to a single
        memory block allocated by Allocate.  However, in some cases the
        implementation may choose to associate more than one memory block
        with a given pool element.

12   For every access subtype S, the following attributes are defined:

13  S'Storage_Pool
                Denotes the storage pool of the type of S. The type of this
                attribute is Root_Storage_Pool'Class.

14  S'Storage_Size
                Yields the result of calling Storage_Size(S'Storage_Pool)[,
                which is intended to be a measure of the number of storage
                elements reserved for the pool.]  The type of this attribute
                is universal_integer.

14.a    Ramification:  Storage_Size is also defined for task subtypes and
        objects -- see 13.3.

14.b    Storage_Size is not a measure of how much un-allocated space is left
        in the pool.  That is, it includes both allocated and unallocated
        space.  Implementations and users may provide a Storage_Available
        function for their pools, if so desired.

15   {specifiable [of Storage_Size for a non-derived access-to-object type]}
{specifiable [of Storage_Pool for a non-derived access-to-object type]}
{Storage_Pool clause} {Storage_Size clause} Storage_Size or Storage_Pool may
be specified for a non-derived access-to-object type via an attribute_
definition_clause; the name in a Storage_Pool clause shall denote a variable.

16   An allocator of type T allocates storage from T's storage pool.  If the
storage pool is a user-defined object, then the storage is allocated by
calling Allocate, passing T'Storage_Pool as the Pool parameter.  The Size_In_
Storage_Elements parameter indicates the number of storage elements to be
allocated, and is no more than D'Max_Size_In_Storage_Elements, where D is the
designated subtype.  The Alignment parameter is D'Alignment.  {contiguous
representation [partial]} {discontiguous representation [partial]} The result
returned in the Storage_Address parameter is used by the allocator as the
address of the allocated storage, which is a contiguous block of memory of
Size_In_Storage_Elements storage elements.  [Any exception propagated by
Allocate is propagated by the allocator.]

        16.a   Ramification:  If the implementation chooses to represent the
        designated subtype in multiple pieces, one allocator evaluation might
        result in more than one call upon Allocate.  In any case, allocators
        for the access type obtain all the required storage for an object of
        the designated type by calling the specified Allocate procedure.

        16.b   Note that the implementation does not turn other exceptions
        into Storage_Error.

17   {standard storage pool} If Storage_Pool is not specified for a type
defined by an access_to_object_definition, then the implementation chooses a
standard storage pool for it in an implementation-defined manner.  {Storage_
Check [partial]} {check, language-defined (Storage_Check)} {Storage_Error
(raised by failure of run-time check)} In this case, the exception Storage_
Error is raised by an allocator if there is not enough storage.  It is
implementation defined whether or not the implementation provides
user-accessible names for the standard pool type(s).

        17.a   Implementation defined:  The manner of choosing a storage pool
        for an access type when Storage_Pool is not specified for the type.

        17.b   Implementation defined:  Whether or not the implementation
        provides user-accessible names for the standard pool type(s).

        17.c   Ramification:  An anonymous access type has no pool.  An
        access-to-object type defined by a derived_type_definition inherits
        its pool from its parent type, so all access-to-object types in the
        same derivation class share the same pool.  Hence the ``defined by an
        access_to_object_definition'' wording above.

        17.d   {contiguous representation [partial]} {discontiguous
        representation [partial]} There is no requirement that all storage
        pools be implemented using a contiguous block of memory (although
        each allocation returns a pointer to a contiguous block of memory).

18   If Storage_Size is specified for an access type, then the Storage_Size
of this pool is at least that requested, and the storage for the pool is
reclaimed when the master containing the declaration of the access type is
left.  {Storage_Error (raised by failure of run-time check)} If the
implementation cannot satisfy the request, Storage_Error is raised at the
point of the attribute_definition_clause.  If neither Storage_Pool nor
Storage_Size are specified, then the meaning of Storage_Size is
implementation defined.

        18.a   Implementation defined:  The meaning of Storage_Size.

        18.b   Ramification:  The Storage_Size function and attribute will
        return the actual size, rather than the requested size.  Comments
        about rounding up, zero, and negative on task Storage_Size apply
        here, as well.  See also AI-00557, AI-00558, and AI-00608.

        18.c   The expression in a Storage_Size clause need not be static.

        18.d   The reclamation happens after the master is finalized.

        18.e   Implementation Note:  For a pool allocated on the stack,
        normal stack cut-back can accomplish the reclamation.  For a
        library-level pool, normal partition termination actions can
        accomplish the reclamation.

19   If Storage_Pool is specified for an access type, then the specified pool
is used.

20   {unspecified [partial]} The effect of calling Allocate and Deallocate
for a standard storage pool directly (rather than implicitly via an allocator
or an instance of Unchecked_Deallocation) is unspecified.

        20.a   Ramification:  For example, an allocator might put the pool
        element on a finalization list.  If the user directly Deallocates it,
        instead of calling an instance of Unchecked_Deallocation, then the
        implementation would probably try to finalize the object upon master
        completion, which would be bad news.  Therefore, the implementation
        should define such situations as erroneous.


                             Erroneous Execution

21   {erroneous execution} If Storage_Pool is specified for an access type,
then if Allocate can satisfy the request, it should allocate a contiguous
block of memory, and return the address of the first storage element in
Storage_Address.  The block should contain Size_In_Storage_Elements storage
elements, and should be aligned according to Alignment.  The allocated
storage should not be used for any other purpose while the pool element
remains in existence.  If the request cannot be satisfied, then Allocate
should propagate an exception [(such as Storage_Error)].  If Allocate behaves
in any other manner, then the program execution is erroneous.


                         Documentation Requirements

22   {documentation requirements} An implementation shall document the set of
values that a user-defined Allocate procedure needs to accept for the
Alignment parameter.  An implementation shall document how the standard
storage pool is chosen, and how storage is allocated by standard storage
pools.

        22.a   Implementation defined:  Implementation-defined aspects of
        storage pools.


                            Implementation Advice

23   An implementation should document any cases in which it dynamically
allocates heap storage for a purpose other than the evaluation of an
allocator.

        23.a   Reason:  This is ``Implementation Advice'' because the term
        ``heap storage'' is not formally definable; therefore, it is not
        testable whether the implementation obeys this advice.

24   A default (implementation-provided) storage pool for an access-to-
constant type should not have overhead to support deallocation of individual
objects.

        24.a   Ramification:  Unchecked_Deallocation is not defined for such
        types.  If the access-to-constant type is library-level, then no
        deallocation (other than at partition completion) will ever be
        necessary, so if the size needed by an allocator of the type is known
        at link-time, then the allocation should be performed statically.
        If, in addition, the initial value of the designated object is known
        at compile time, the object can be allocated to read-only memory.

        24.b   Implementation Note:  If the Storage_Size for an access type
        is specified, the storage pool should consist of a contiguous block
        of memory, possibly allocated on the stack.  The pool should contain
        approximately this number of storage elements.  These storage
        elements should be reserved at the place of the Storage_Size clause,
        so that allocators cannot raise Storage_Error due to running out of
        pool space until the appropriate number of storage elements has been
        used up.  This approximate (possibly rounded-up) value should be used
        as a maximum; the implementation should not increase the size of the
        pool on the fly.  If the Storage_Size for an access type is specified
        as zero, then the pool should not take up any storage space, and any
        allocator for the type should raise Storage_Error.

        24.c   Ramification:  Note that most of this is approximate, and so
        cannot be (portably) tested.  That's why we make it an Implementation
        Note.  There is no particular number of allocations that is
        guaranteed to succeed, and there is no particular number of
        allocations that is guaranteed to fail.

25   A storage pool for an anonymous access type should be created at the
point of an allocator for the type, and be reclaimed when the designated
object becomes inaccessible.

        25.a   Implementation Note:  Normally the "storage pool" for an
        anonymous access type would not exist as a separate entity.  Instead,
        the designated object of the allocator would be allocated, in the
        case of an access parameter, as a local aliased variable at the call
        site, and in the case of an access discriminant, contiguous with the
        object containing the discriminant.  This is similar to the way
        storage for aggregates is typically managed.


     NOTES
26   (23) A user-defined storage pool type can be obtained by extending the
     Root_Storage_Pool type, and overriding the primitive subprograms
     Allocate, Deallocate, and Storage_Size.  A user-defined storage pool can
     then be obtained by declaring an object of the type extension.  The user
     can override Initialize and Finalize if there is any need for
     non-trivial initialization and finalization for a user-defined pool
     type.  For example, Finalize might reclaim blocks of storage that are
     allocated separately from the pool object itself.

27   (24) The writer of the user-defined allocation and deallocation
     procedures, and users of allocators for the associated access type, are
     responsible for dealing with any interactions with tasking.  In
     particular:

        28  If the allocators are used in different tasks, they require
            mutual exclusion.

        29  If they are used inside protected objects, they cannot
            block.

        30  If they are used by interrupt handlers (see C.3, ``Interrupt
            Support''), the mutual exclusion mechanism has to work
            properly in that context.

31   (25) The primitives Allocate, Deallocate, and Storage_Size are declared
     as abstract (see 3.9.3), and therefore they have to be overridden when a
     new (non-abstract) storage pool type is declared.

   31.a   Ramification:  Note that the Storage_Pool attribute denotes an
        object, rather than a value, which is somewhat unusual for
        attributes.

   31.b   The calls to Allocate, Deallocate, and Storage_Size are dispatching
        calls -- this follows from the fact that the actual parameter for
        Pool is T'Storage_Pool, which is of type Root_Storage_Pool'Class.  In
        many cases (including all cases in which Storage_Pool is not
        specified), the compiler can determine the tag statically.  However,
        it is possible to construct cases where it cannot.

   31.c   All access types in the same derivation class share the same pool,
        whether implementation defined or user defined.  This is necessary
        because we allow type conversions among them (even if they are
        pool-specific), and we want pool-specific access values to always
        designate an element of the right pool.

   31.d   Implementation Note:  If an access type has a standard storage
        pool, then the implementation doesn't actually have to follow the
        pool interface described here, since this would be semantically
        invisible.  For example, the allocator could conceivably be
        implemented with inline code.


                                  Examples

32   To associate an access type with a storage pool object, the user first
declares a pool object of some type derived from Root_Storage_Pool.  Then,
the user defines its Storage_Pool attribute, as follows:

33  Pool_Object : Some_Storage_Pool_Type;

34  type T is access Designated;
    for T'Storage_Pool use Pool_Object;

35   Another access type may be added to an existing storage pool, via:

36  for T2'Storage_Pool use T'Storage_Pool;

37   The semantics of this is implementation defined for a standard storage
pool.

        37.a   Reason:  For example, the implementation is allowed to choose
        a storage pool for T that takes advantage of the fact that T is of a
        certain size.  If T2 is not of that size, then the above will
        probably not work.

38   As usual, a derivative of Root_Storage_Pool may define additional
operations.  For example, presuming that Mark_Release_Pool_Type has two
additional operations, Mark and Release, the following is a possible use:

39  type Mark_Release_Pool_Type
       (Pool_Size : Storage_Elements.Storage_Count;
        Block_Size : Storage_Elements.Storage_Count)
            is new Root_Storage_Pool with limited private;

40  ...

41
    MR_Pool : Mark_Release_Pool_Type (Pool_Size => 2000,
                                      Block_Size => 100);

42  type Acc is access ...;
    for Acc'Storage_Pool use MR_Pool;
    ...

43  Mark(MR_Pool);
    ... -- Allocate objects using ``new Designated(...)''.
    Release(MR_Pool); -- Reclaim the storage.


                            Extensions to Ada 83
        43.a   {extensions to Ada 83} User-defined storage pools are new to
        Ada 9X.

                         Wording Changes From Ada 83

        43.b   Ada 83 had a concept called a ``collection,'' which is similar
        to what we call a storage pool.  All access types in the same
        derivation class shared the same collection.  In Ada 9X, all access
        types in the same derivation class share the same storage pool, but
        other (unrelated) access types can also share the same storage pool,
        either by default, or as specified by the user.  A collection was an
        amorphous collection of objects; a storage pool is a more concrete
        concept -- hence the different name.

        43.c   RM83 states the erroneousness of reading or updating
        deallocated objects incorrectly by missing various cases.



13.11.1 The Max_Size_In_Storage_Elements Attribute

1   [The Max_Size_In_Storage_Elements attribute is useful in writing
user-defined pool types.]


                              Static Semantics

2   For every subtype S, the following attribute is defined:

3   S'Max_Size_In_Storage_Elements
                Denotes the maximum value for Size_In_Storage_Elements that
                will be requested via Allocate for an access type whose
                designated subtype is S. The value of this attribute is of
                type universal_integer.

3.a     Ramification:  If S is an unconstrained array subtype, or an
        unconstrained subtype with discriminants, S'Max_Size_In_Storage_
        Elements might be very large.



13.11.2 Unchecked Storage Deallocation

1   [{unchecked storage deallocation} {storage deallocation (unchecked)}
{deallocation of storage} {reclamation of storage} {freeing storage}
Unchecked storage deallocation of an object designated by a value of an
access type is achieved by a call to an instance of the generic procedure
Unchecked_Deallocation.]


                              Static Semantics

2   The following language-defined generic library procedure exists:

3   generic
       type Object(<>) is limited private;
       type Name   is access  Object;
    procedure Ada.Unchecked_Deallocation(X : in out Name);
    pragma Convention(Intrinsic, Ada.Unchecked_Deallocation);
    pragma Preelaborate(Ada.Unchecked_Deallocation);

{94-4893.a}

        3.a   Reason:  The pragma Convention implies that the attribute
        Access is not allowed for instances of Unchecked_Deallocation.


                              Dynamic Semantics

4   Given an instance of Unchecked_Deallocation declared as follows:

5   procedure Free is
        new Ada.Unchecked_Deallocation(
            object_subtype_name, access_to_variable_subtype_name);

6   Procedure Free has the following effect:

    7  After executing Free(X), the value of X is null.

    8  Free(X), when X is already equal to null, has no effect.

    9  Free(X), when X is not equal to null first performs finalization,
       as described in 7.6.  It then deallocates the storage occupied by
       the object designated by X. If the storage pool is a user-defined
       object, then the storage is deallocated by calling Deallocate,
       passing access_to_variable_subtype_name'Storage_Pool as the Pool
       parameter.  Storage_Address is the value returned in the Storage_
       Address parameter of the corresponding Allocate call.  Size_In_
       Storage_Elements and Alignment are the same values passed to the
       corresponding Allocate call.  There is one exception: if the
       object being freed contains tasks, the object might not be
       deallocated.

 9.a    Ramification:  Free calls only the specified Deallocate
        procedure to do deallocation.  For any given object
        deallocation, the number of calls to Free (usually one) will be
        equal to the number of Allocate calls it took to allocate the
        object.  We do not define the relative order of multiple calls
        used to deallocate the same object -- that is, if the allocator
        allocated two pieces x and y, then Free might deallocate x and
        then y, or it might deallocate y and then x.

10   {freed: see nonexistent} {nonexistent} After Free(X), the object
designated by X, and any subcomponents thereof, no longer exist; their
storage can be reused for other purposes.


                          Bounded (Run-Time) Errors

11   {bounded error} It is a bounded error to free a discriminated,
unterminated task object.  The possible consequences are:

        11.a   Reason:  This is an error because the task might refer to its
        discriminants, and the discriminants might be deallocated by freeing
        the task object.

   12  No exception is raised.

   13  {Program_Error (raised by failure of run-time check)} {Tasking_
       Error (raised by failure of run-time check)} Program_Error or
       Tasking_Error is raised at the point of the deallocation.

   14  {Program_Error (raised by failure of run-time check)} {Tasking_
       Error (raised by failure of run-time check)} Program_Error or
       Tasking_Error is raised in the task the next time it references
       any of the discriminants.

 14.a   Implementation Note:  This last case presumes an implementation
        where the task references its discriminants indirectly, and the
        pointer is nulled out when the task object is deallocated.

15   In the first two cases, the storage for the discriminants (and for any
enclosing object if it is designated by an access discriminant of the task)
is not reclaimed prior to task termination.

        15.a   Ramification:  The storage might never be reclaimed.


                             Erroneous Execution

16   {erroneous execution} {nonexistent} Evaluating a name that denotes a
nonexistent object is erroneous.  {94-4791.a} The execution of a call to an
instance of Unchecked_Deallocation is erroneous if the object was created
other than by an allocator for an access type whose pool is Name'Storage_
Pool.


                            Implementation Advice

17   For a standard storage pool, Free should actually reclaim the storage.

        17.a   Ramification:  This is not a testable property, since we do
        not how much storage is used by a given pool element, nor whether
        fragmentation can occur.


     NOTES
18   (26) The rules here that refer to Free apply to any instance of
     Unchecked_Deallocation.

19   (27) Unchecked_Deallocation cannot be instantiated for an access-to-
     constant type.  This is implied by the rules of 12.5.4.



13.11.3 Pragma Controlled

1   [Pragma Controlled is used to prevent any automatic reclamation of
storage (garbage collection) for the objects created by allocators of a given
access type.]


                                   Syntax

    2   The form of a pragma Controlled is as follows:


3     pragma Controlled(first_subtype_local_name);

        3.a   Discussion:  Not to be confused with type Finalization.-
        Controlled.


                               Legality Rules

4   The first_subtype_local_name of a pragma Controlled shall denote a
non-derived access subtype.


                              Static Semantics

5   {representation pragma [Controlled]} {pragma, representation
[Controlled]} A pragma Controlled is a representation pragma {aspect of
representation [controlled]} {controlled (aspect of representation)} that
specifies the controlled aspect of representation.

6   {garbage collection} Garbage collection is a process that automatically
reclaims storage, or moves objects to a different address, while the objects
still exist.
        6.a   Ramification:  Storage reclamation upon leaving a master is not
        considered garbage collection.

        6.b   Note that garbage collection includes compaction of a pool
        (``moved to a different Address''), even if storage reclamation is
        not done.

        6.c   Reason:  Programs that will be damaged by automatic storage
        reclamation are just as likely to be damaged by having objects moved
        to different locations in memory.  A pragma Controlled should turn
        off both flavors of garbage collection.

        6.d   Implementation Note:  If garbage collection reclaims the
        storage of a controlled object, it should first finalize it.
        Finalization is not done when moving an object; any self-relative
        pointers will have to be updated by the garbage collector.  If an
        implementation provides garbage collection for a storage pool
        containing controlled objects (see 7.6), then it should provide a
        means for deferring garbage collection of those controlled objects.

        6.e   Reason:  This allows the manager of a resource released by a
        Finalize operation to defer garbage collection during its critical
        regions; it is up to the author of the Finalize operation to do so.
        Garbage collection, at least in some systems, can happen
        asynchronously with respect to normal user code.  Note that it is not
        enough to defer garbage collection during Initialize, Adjust, and
        Finalize, because the resource in question might be used in other
        situations as well.  For example:

6.f         with Ada.Finalization;
            package P is

6.g             type My_Controlled is
                    new Ada.Finalization.Limited_Controlled with private;
                procedure Finalize(Object : in out My_Controlled);
                type My_Controlled_Access is access My_Controlled;

6.h             procedure Non_Reentrant;

6.i         private
                ...
            end P;

6.j         package body P is
                X : Integer := 0;
                A : array(Integer range 1..10) of Integer;

6.k             procedure Non_Reentrant is
                begin
                    X := X + 1;
                    -- If the system decides to do a garbage collection here,
                    -- then we're in trouble, because it will call Finalize on
                    -- the collected objects; we essentially have two threads
                    -- of control erroneously accessing shared variables.
                    -- The garbage collector behaves like a separate thread
                    -- of control, even though the user hasn't declared
                    -- any tasks.
                    A(X) := ...;
                end Non_Reentrant;

6.l             procedure Finalize(Object : in out My_Controlled) is
                begin
                    Non_Reentrant;
                end Finalize;
            end P;

6.m         with P; use P;
            procedure Main is
            begin
                ... new My_Controlled ... -- allocate some objects
                ...  forget the pointers to some of them, so they become garbage
                Non_Reentrant;
            end Main;

        6.n   It is the user's responsibility to protect against this sort of
        thing, and the implementation's responsibility to provide the
        necessary operations.

        6.o   We do not give these operations names, nor explain their exact
        semantics, because different implementations of garbage collection
        might have different needs, and because garbage collection is not
        supported by most Ada implementations, so portability is not
        important here.  Another reason not to turn off garbage collection
        during each entire Finalize operation is that it would create a
        serial bottleneck; it might be only part of the Finalize operation
        that conflicts with some other resource.  It is the intention that
        the mechanisms provided be finer-grained than pragma Controlled.

7   If a pragma Controlled is specified for an access type with a standard
storage pool, then garbage collection is not performed for objects in that
pool.

        7.a   Ramification:  If Controlled is not specified, the
        implementation may, but need not, perform garbage collection.  If
        Storage_Pool is specified, then a pragma Controlled for that type is
        ignored.

        7.b   Reason:  Controlled means that implementation-provided garbage
        collection is turned off; if the Storage_Pool is specified, the pool
        controls whether garbage collection is done.


                         Implementation Permissions

8   An implementation need not support garbage collection, in which case, a
pragma Controlled has no effect.


                         Wording Changes From Ada 83

        8.a   Ada 83 used the term ``automatic storage reclamation'' to refer
        to what is known traditionally as ``garbage collection''.  Because of
        the existence of storage pools (see 13.11), we need to distinguish
        this from the storage reclamation that might happen upon leaving a
        master.  Therefore, we now use the term ``garbage collection'' in its
        normal computer-science sense.  This has the additional advantage of
        making our terminology more accessible to people outside the Ada
        world.



13.12 Pragma Restrictions

1   [A pragma Restrictions expresses the user's intent to abide by certain
restrictions.  This may facilitate the construction of simpler run-time
environments.]


                                   Syntax

    2   The form of a pragma Restrictions is as follows:


3     pragma Restrictions(restriction{, restriction});

4   restriction ::= restriction_identifier
        | restriction_parameter_identifier => expression


                            Name Resolution Rules

5   {expected type [restriction parameter expression]} Unless otherwise
specified for a particular restriction, the expression is expected to be of
any integer type.


                               Legality Rules

6   Unless otherwise specified for a particular restriction, the expression
shall be static, and its value shall be nonnegative.


                              Static Semantics

7   The set of restrictions is implementation defined.

        7.a   Implementation defined:  The set of restrictions allowed in a
        pragma Restrictions.


                           Post-Compilation Rules

8   {post-compilation rules} {configuration pragma [Restrictions]} {pragma,
configuration [Restrictions]} A pragma Restrictions is a configuration
pragma; unless otherwise specified for a particular restriction, a partition
shall obey the restriction if a pragma Restrictions applies to any
compilation unit included in the partition.


                         Implementation Permissions

9   An implementation may place limitations on the values of the expression
that are supported, and limitations on the supported combinations of
restrictions.  The consequences of violating such limitations are
implementation defined.

        9.a   Implementation defined:  The consequences of violating
        limitations on Restrictions pragmas.

        9.b   Ramification:  Such limitations may be enforced at compile time
        or at run time.  Alternatively, the implementation is allowed to
        declare violations of the restrictions to be erroneous, and not
        enforce them at all.


     NOTES
10   (28) Restrictions intended to facilitate the construction of efficient
     tasking run-time systems are defined in D.7.  Safety- and
     security-related restrictions are defined in H.4.

11   (29) An implementation has to enforce the restrictions in cases where
     enforcement is required, even if it chooses not to take advantage of the
     restrictions in terms of efficiency.

   11.a   Discussion:  It is not the intent that an implementation will
        support a different run-time system for every possible combination of
        restrictions.  An implementation might support only two run-time
        systems, and document a set of restrictions that is sufficient to
        allow use of the more efficient and safe one.
                            Extensions to Ada 83

        11.b   {extensions to Ada 83} Pragma Restrictions is new to Ada 9X.



13.13 Streams

1   {stream} {stream type} A stream is a sequence of elements comprising
values from possibly different types and allowing sequential access to these
values.  A stream type is a type in the class whose root type is
Streams.Root_Stream_Type.  A stream type may be implemented in various ways,
such as an external sequential file, an internal buffer, or a network
channel.

        1.a   Discussion:  A stream element will often be the same size as a
        storage element, but that is not required.


                            Extensions to Ada 83

        1.b   {extensions to Ada 83} Streams are new in Ada 9X.



13.13.1 The Package Streams

                              Static Semantics

1   The abstract type Root_Stream_Type is the root type of the class of
stream types.  The types in this class represent different kinds of streams.
A new stream type is defined by extending the root type (or some other stream
type), overriding the Read and Write operations, and optionally defining
additional primitive subprograms, according to the requirements of the
particular kind of stream.  The predefined stream-oriented attributes like
T'Read and T'Write make dispatching calls on the Read and Write procedures of
the Root_Stream_Type.  (User-defined T'Read and T'Write attributes can also
make such calls, or can call the Read and Write attributes of other types.)

2   package Ada.Streams is
        pragma Pure(Streams){unpolluted} ;

3       type Root_Stream_Type is abstract tagged limited private;

4       type Stream_Element is mod implementation-defined;
        type Stream_Element_Offset is range implementation-defined;
        subtype Stream_Element_Count is
            Stream_Element_Offset range 0..Stream_Element_Offset'Last;
        type Stream_Element_Array is
            array(Stream_Element_Offset range <>) of Stream_Element;

5       procedure Read(
          Stream : in out Root_Stream_Type;
          Item   : out Stream_Element_Array;
          Last   : out Stream_Element_Offset) is abstract;

6       procedure Write(
          Stream : in out Root_Stream_Type;
          Item   : in Stream_Element_Array) is abstract;

7   private
       ... -- not specified by the language
    end Ada.Streams;

8   The Read operation transfers Item'Length stream elements from the
specified stream to fill the array Item.  The index of the last stream
element transferred is returned in Last.  Last is less than Item'Last only if
the end of the stream is reached.

9   The Write operation appends Item to the specified stream.


     NOTES
10   (30) See A.12.1, ``The Package Streams.Stream_IO'' for an example of
     extending type Root_Stream_Type.



13.13.2 Stream-Oriented Attributes

1   The Write, Read, Output, and Input attributes convert values to a stream
of elements and reconstruct values from a stream.


                              Static Semantics

2   For every subtype S of a specific type T, the following attributes are
defined.  {94-4810.a}

3   S'Write
                S'Write denotes a procedure with the following specification:

4                   procedure S'Write(
                       Stream : access Ada.Streams.Root_Stream_Type'Class;
                       Item : in T)

                5   S'Write writes the value of Item to Stream.

6   S'Read
                S'Read denotes a procedure with the following specification:

7                   procedure S'Read(
                       Stream : access Ada.Streams.Root_Stream_Type'Class;
                       Item : out T)

                8   S'Read reads the value of Item from Stream.

9   For elementary types, the representation in terms of stream elements is
implementation defined.  For composite types, the Write or Read attribute for
each component is called in a canonical order.  The canonical order of
components is last dimension varying fastest for an array, and positional
aggregate order for a record.  Bounds are not included in the stream if T is
an array type.  If T is a discriminated type, discriminants are included only
if they have defaults.  If T is a tagged type, the tag is not included.
{94-4855.a}

        9.a   Implementation defined:  The representation used by the Read
        and Write attributes of elementary types in terms of stream elements.

        9.b   Reason:  A discriminant with a default value is treated simply
        as a component of the object.  On the other hand, an array bound or a
        discriminant without a default value, is treated as ``descriptor'' or
        ``dope'' that must be provided in order to create the object and thus
        is logically separate from the regular components.  Such
        ``descriptor'' data are written by 'Output and produced as part of
        the delivered result by the 'Input function, but they are not written
        by 'Write nor read by 'Read.  A tag is like a discriminant without a
        default.

        9.c   Ramification:  For a composite object, the subprogram denoted
        by the Write or Read attribute of each component is called, whether
        it is the default or is user-specified.

10   For every subtype S'Class of a class-wide type T'Class:

11  S'Class'Write
                S'Class'Write denotes a procedure with the following
                specification:

12                  procedure S'Class'Write(
                       Stream : access Ada.Streams.Root_Stream_Type'Class;
                       Item   : in T'Class)

                13   Dispatches to the subprogram denoted by the Write
                attribute of the specific type identified by the tag of Item.
                {94-4810.a}

14  S'Class'Read
                S'Class'Read denotes a procedure with the following
                specification:

15                  procedure S'Class'Read(
                       Stream : access Ada.Streams.Root_Stream_Type'Class;
                       Item : out T'Class)

                16   Dispatches to the subprogram denoted by the Read
                attribute of the specific type identified by the tag of Item.
                {94-4810.a}

16.a    Reason:  It is necessary to have class-wide versions of Read and
        Write in order to avoid generic contract model violations; in a
        generic, we don't necessarily know at compile time whether a given
        type is specific or class-wide.


                            Implementation Advice

17   If a stream element is the same size as a storage element, then the
normal in-memory representation should be used by Read and Write for scalar
objects.  Otherwise, Read and Write should use the smallest number of stream
elements needed to represent all values in the base range of the scalar type.
{94-4855.a}


                              Static Semantics

18   For every subtype S of a specific type T, the following attributes are
defined.  {94-4810.a}

19  S'Output
                S'Output denotes a procedure with the following specifica-
                tion:

20                  procedure S'Output(
                       Stream : access Ada.Streams.Root_Stream_Type'Class;
                       Item : in T)

                21   S'Output writes the value of Item to Stream, including
                any bounds or discriminants.

21.a    Ramification:  Note that the bounds are included even for an array
        type whose first subtype is constrained.

22  S'Input
                S'Input denotes a function with the following specification:

23                  function S'Input(
                       Stream : access Ada.Streams.Root_Stream_Type'Class)
                       return T

                24   S'Input reads and returns one value from Stream, using
                any bounds or discriminants written by a corresponding
                S'Output to determine how much to read.

25   Unless overridden by an attribute_definition_clause, these subprograms
execute as follows:  {94-4810.a}

   26  If T is an array type, S'Output first writes the bounds, and
       S'Input first reads the bounds.  If T has discriminants without
       defaults, S'Output first writes the discriminants (using S'Write
       for each), and S'Input first reads the discriminants (using
       S'Read for each).

   27  S'Output then calls S'Write to write the value of Item to the
       stream.  S'Input then creates an object (with the bounds or
       discriminants, if any, taken from the stream), initializes it
       with S'Read, and returns the value of the object.

28   For every subtype S'Class of a class-wide type T'Class:

29  S'Class'Output
                S'Class'Output denotes a procedure with the following
                specification:

30                  procedure S'Class'Output(
                       Stream : access Ada.Streams.Root_Stream_Type'Class;
                       Item   : in T'Class)

                31   First writes the external tag of Item to Stream (by
                calling String'Output(Tags.External_Tag(Item'Tag) -- see 3.9)
                and then dispatches to the subprogram denoted by the Output
                attribute of the specific type identified by the tag.

32  S'Class'Input
                S'Class'Input denotes a function with the following
                specification:

33                  function S'Class'Input(
                       Stream : access Ada.Streams.Root_Stream_Type'Class)
                       return T'Class

                {94-4768.u}

                34   First reads the external tag from Stream and determines
                the corresponding internal tag (by calling Tags.Internal_
                Tag(String'Input(Stream)) -- see 3.9) and then dispatches to
                the subprogram denoted by the Input attribute of the specific
                type identified by the internal tag; returns that result.

35   {Range_Check [partial]} {check, language-defined (Range_Check)} In the
default implementation of Read and Input for a composite type, for each
scalar component that is a discriminant or whose component_declaration
includes a default_expression, a check is made that the value returned by
Read for the component belongs to its subtype.  {Constraint_Error (raised by
failure of run-time check)} Constraint_Error is raised if this check fails.
For other scalar components, no check is made.  For each component that is of
an access type, if the implementation can detect that the value returned by
Read for the component is not a value of its subtype, Constraint_Error is
raised.  If the value is not a value of its subtype and this error is not
detected, the component has an abnormal value, and erroneous execution can
result (see 13.9.1).

36   {specifiable [of Read for a type]} {specifiable [of Write for a type]}
{specifiable [of Input for a type]} {specifiable [of Output for a type]}
{Read clause} {Write clause} {Input clause} {Output clause} The
stream-oriented attributes may be specified for any type via an attribute_
definition_clause.  All nonlimited types have default implementations for
these operations.  An attribute_reference for one of these attributes is
illegal if the type is limited, unless the attribute has been specified by an
attribute_definition_clause.  For an attribute_definition_clause specifying
one of these attributes, the subtype of the Item parameter shall be the base
subtype if scalar, and the first subtype otherwise.  The same rule applies to
the result of the Input function.  {94-4810.a}

        36.a   Reason:  This is to simplify implementation.


     NOTES
37   (31) For a definite subtype S of a type T, only T'Write and T'Read are
     needed to pass an arbitrary value of the subtype through a stream.  For
     an indefinite subtype S of a type T, T'Output and T'Input will normally
     be needed, since T'Write and T'Read do not pass bounds, discriminants,
     or tags.  {94-4855.a}

38   (32) User-specified attributes of S'Class are not inherited by other
     class-wide types descended from S. {94-4969.a}


                                  Examples

39   Example of user-defined Write attribute:

40  procedure My_Write(
      Stream : access Ada.Streams.Root_Stream_Type'Class; Item : My_Integer'Bas\
e);
    for My_Integer'Write use My_Write;

        40.a   Discussion:  Example of network input/output using input
        output attributes:

40.b        with Ada.Streams; use Ada.Streams;
            generic
                type Msg_Type(<>) is private;
            package Network_IO is
                -- Connect/Disconnect are used to establish the stream
                procedure Connect(...);
                procedure Disconnect(...);

40.c            -- Send/Receive transfer messages across the network
                procedure Send(X : in Msg_Type);
                function Receive return Msg_Type;
            private
                type Network_Stream is new Root_Stream_Type with ...
                procedure Read(...);  -- define Read/Write for Network_Stream
                procedure Write(...);
            end Network_IO;

40.d        with Ada.Streams; use Ada.Streams;
            package body Network_IO is
                Current_Stream : aliased Network_Stream;
                . . .
                procedure Connect(...) is ...;
                procedure Disconnect(...) is ...;

40.e            procedure Send(X : in Msg_Type) is
                begin
                    Msg_Type'Output(Current_Stream'Access, X);
                end Send;

40.f            function Receive return Msg_Type is
                begin
                    return Msg_Type'Input(Current_Stream'Access);
                end Receive;
            end Network_IO;



13.14 Freezing Rules

1   [This clause defines a place in the program text where each declared
entity becomes ``frozen.''  A use of an entity, such as a reference to it by
name, or (for a type) an expression of the type, causes freezing of the
entity in some contexts, as described below.  The Legality Rules forbid
certain kinds of uses of an entity in the region of text where it is frozen.]

        1.a   Reason:  This concept has two purposes: a compile-time one and
        a run-time one.

        1.b   The compile-time purpose of the freezing rules comes from the
        fact that the evaluation of static expressions depends on overload
        resolution, and overload resolution sometimes depends on the value of
        a static expression.  (The dependence of static evaluation upon
        overload resolution is obvious.  The dependence in the other
        direction is more subtle.  There are three rules that require static
        expressions in contexts that can appear in declarative places:  The
        expression in an attribute_designator shall be static.  In a record
        aggregate, variant-controlling discriminants shall be static.  In an
        array aggregate with more than one named association, the choices
        shall be static.  The compiler needs to know the value of these
        expressions in order to perform overload resolution and legality
        checking.)  We wish to allow a compiler to evaluate static
        expressions when it sees them in a single pass over the compilation_
        unit.  The freezing rules ensure that.

        1.c   The run-time purpose of the freezing rules is called the
        ``linear elaboration model.''  This means that declarations are
        elaborated in the order in which they appear in the program text, and
        later elaborations can depend on the results of earlier ones.  The
        elaboration of the declarations of certain entities requires run-time
        information about the implementation details of other entities.  The
        freezing rules ensure that this information has been calculated by
        the time it is used.  For example, suppose the initial value of a
        constant is the result of a function call that takes a parameter of
        type T.  In order to pass that parameter, the size of type T has to
        be known.  If T is composite, that size might be known only at run
        time.

        1.d   (Note that in these discussions, words like ``before'' and
        ``after'' generally refer to places in the program text, as opposed
        to times at run time.)

        1.e   Discussion:  The ``implementation details'' we're talking about
        above are:

          1.f  For a tagged type, the implementations of all the
               primitive subprograms of the type -- that is (in the
               canonical implementation model), the contents of the type
               descriptor, which contains pointers to the code for each
               primitive subprogram.

          1.g  For a type, the full type declaration of any parts
               (including the type itself) that are private.

          1.h  For a deferred constant, the full constant declaration,
               which gives the constant's value.  (Since this
               information necessarily comes after the constant's type
               and subtype are fully known, there's no need to worry
               about its type or subtype.)

          1.i  For any entity, representation information specified by
               the user via representation items.  Most representation
               items are for types or subtypes; however, various other
               kinds of entities, such as objects and subprograms, are
               possible.

        1.j   Similar issues arise for incomplete types.  However, we do not
        use freezing there; incomplete types have different, more severe,
        restrictions.  Similar issues also arise for subprograms, protected
        operations, tasks and generic units.  However, we do not use freezing
        there either; 3.11 prevents problems with run-time Elaboration_
        Checks.


                         Language Design Principles

        1.k   An evaluable construct should freeze anything that's needed to
        evaluate it.

        1.l   However, if the construct is not evaluated where it appears,
        let it cause freezing later, when it is evaluated.  This is the case
        for default_expressions and default_names.  (Formal parameters,
        generic formal parameters, and components can have default_
        expressions or default_names.)

        1.m   The compiler should be allowed to evaluate static expressions
        without knowledge of their context.  (I.e. there should not be any
        special rules for static expressions that happen to occur in a
        context that requires a static expression.)

        1.n   Compilers should be allowed to evaluate static expressions (and
        record the results) using the run-time representation of the type.
        For example, suppose Color'Pos(Red) = 1, but the internal code for
        Red is 37.  If the value of a static expression is Red, some
        compilers might store 1 in their symbol table, and other compilers
        might store 37.  Either compiler design should be feasible.

        1.o   Compilers should never be required to detect erroneousness or
        exceptions at compile time (although it's very nice if they do).
        This implies that we should not require code-generation for a
        nonstatic expression of type T too early, even if we can prove that
        that expression will be erroneous, or will raise an exception.

        1.p   Here's an example (modified from AI-00039, Example 3):

1.q         type T is
                record
                    ...
                end record;
            function F return T;
            function G(X : T) return Boolean;
            Y : Boolean := G(F); -- doesn't force T in Ada 83
            for T use
                record
                    ...
                end record;

        1.r   AI-00039 says this is legal.  Of course, it raises Program_
        Error because the function bodies aren't elaborated yet.  A one-pass
        compiler has to generate code for an expression of type T before it
        knows the representation of T. Here's a similar example, which
        AI-00039 also says is legal:

1.s         package P is
                type T is private;
                function F return T;
                function G(X : T) return Boolean;
                Y : Boolean := G(F); -- doesn't force T in Ada 83
            private
                type T is
                    record
                        ...
                    end record;
            end P;

        1.t   If T's size were dynamic, that size would be stored in some
        compiler-generated dope; this dope would be initialized at the place
        of the full type declaration.  However, the generated code for the
        function calls would most likely allocate a temp of the size
        specified by the dope before checking for Program_Error.  That dope
        would contain uninitialized junk, resulting in disaster.  To avoid
        doing that, the compiler would have to determine, at compile time,
        that the expression will raise Program_Error.

        1.u   This is silly.  If we're going to require compilers to detect
        the exception at compile time, we might as well formulate the rule as
        a legality rule.

        1.v   Compilers should not be required to generate code to load the
        value of a variable before the address of the variable has been
        determined.

        1.w   After an entity has been frozen, no further requirements may be
        placed on its representation (such as by a representation item or a
        full_type_declaration).
2   {freezing (entity) [distributed]} {freezing points (entity)} The freezing
of an entity occurs at one or more places (freezing points) in the program
text where the representation for the entity has to be fully determined.
Each entity is frozen from its first freezing point to the end of the program
text (given the ordering of compilation units defined in 10.1.4).

        2.a   Ramification:  The ``representation'' for a subprogram includes
        its calling convention and means for referencing the subprogram body,
        either a ``link-name'' or specified address.  It does not include the
        code for the subprogram body itself, nor its address if a link-name
        is used to reference the body.

3   {freezing (entity caused by the end of an enclosing construct)} The end
of a declarative_part, protected_body, or a declaration of a library package
or generic library package, causes freezing of each entity declared within
it, except for incomplete types.  {freezing (entity caused by a body)} A
noninstance body causes freezing of each entity declared before it within the
same declarative_part.

        3.a   Discussion:  This is worded carefully to handle nested packages
        and private types.  Entities declared in a nested package_
        specification will be frozen by some containing construct.

        3.b   An incomplete type declared in the private part of a library
        package_specification can be completed in the body.

        3.c   Ramification:  The part about bodies does not say immediately
        within.  A renaming-as-body does not have this property.  Nor does a
        pragma Import.

        3.d   Reason:  The reason bodies cause freezing is because we want
        proper_bodies and body_stubs to be interchangeable -- one should be
        able to move a proper_body to a subunit, and vice-versa, without
        changing the semantics.  Clearly, anything that should cause freezing
        should do so even if it's inside a proper_body.  However, if we make
        it a body_stub, then the compiler can't see that thing that should
        cause freezing.  So we make body_stubs cause freezing, just in case
        they contain something that should cause freezing.  But that means we
        need to do the same for proper_bodies.

        3.e   Another reason for bodies to cause freezing, there could be an
        added implementation burden if an entity declared in an enclosing
        declarative_part is frozen within a nested body, since some compilers
        look at bodies after looking at the containing declarative_part.

4   {freezing (entity caused by a construct) [distributed]} A construct that
(explicitly or implicitly) references an entity can cause the freezing of the
entity, as defined by subsequent paragraphs.  {freezing [by a constituent of
a construct]} At the place where a construct causes freezing, each name,
expression[, or range] within the construct causes freezing:

        4.a   Ramification:  Note that in the sense of this paragraph, a
        subtype_mark ``references'' the denoted subtype, but not the type.

    5  {freezing [generic_instantiation]} The occurrence of a generic_
       instantiation causes freezing; also, if a parameter of the
       instantiation is defaulted, the default_expression or default_
       name for that parameter causes freezing.

    6  {freezing [object_declaration]} The occurrence of an object_
       declaration that has no corresponding completion causes freezing.

 6.a    Ramification:  Note that this does not include a formal_object_
        declaration.

    7  {freezing [subtype caused by a record extension]} The declaration
       of a record extension causes freezing of the parent subtype.

 7.a    Ramification:  This combined with another rule specifying that
        primitive subprogram declarations shall precede freezing ensures
        that all descendants of a tagged type implement all of its
        dispatching operations.

 7.b    The declaration of a private extension does not cause freezing.
        The freezing is deferred until the full type declaration, which
        will necessarily be for a record extension.

8   {freezing [by an expression]} A static expression causes freezing where
it occurs.  A nonstatic expression causes freezing where it occurs, unless
the expression is part of a default_expression, a default_name, or a
per-object expression of a component's constraint, in which case, the
freezing occurs later as part of another construct.

9   The following rules define which entities are frozen at the place where a
construct causes freezing:

   10  {freezing [type caused by an expression]} At the place where an
       expression causes freezing, the type of the expression is frozen,
       unless the expression is an enumeration literal used as a
       discrete_choice of the array_aggregate of an enumeration_
       representation_clause.

 10.a   Reason:  We considered making enumeration literals never cause
        freezing, which would be more upward compatible, but examples
        like the variant record aggregate (Discrim => Red, ...)  caused
        us to change our mind.  Furthermore, an enumeration literal is a
        static expression, so the implementation should be allowed to
        represent it using its representation.

 10.b   Ramification:  The following pathological example was legal in
        Ada 83, but is illegal in Ada 9X:

10.c        package P1 is
                type T is private;
                package P2 is
                    type Composite(D : Boolean) is
                        record
                            case D is
                                when False => Cf : Integer;
                                when True  => Ct : T;
                            end case;
                        end record;
                end P2;
                X : Boolean := P2."="( (False,1), (False,1) );
            private
                type T is array(1..Func_Call) of Integer;
            end;

 10.d   In Ada 9X, the declaration of X freezes Composite (because it
        contains an expression of that type), which in turn freezes T
        (even though Ct does not exist in this particular case).  But
        type T is not completely defined at that point, violating the
        rule that a type shall be completely defined before it is
        frozen.  In Ada 83, on the other hand, there is no occurrence of
        the name T, hence no forcing occurrence of T.

   11  {freezing [entity caused by a name]} At the place where a name
       causes freezing, the entity denoted by the name is frozen, unless
       the name is a prefix of an expanded name; {freezing [nominal
       subtype caused by a name]} at the place where an object name
       causes freezing, the nominal subtype associated with the name is
       frozen.

 11.a   Ramification:  This only matters in the presence of deferred
        constants or access types; an object_declaration other than a
        deferred_constant_declaration causes freezing of the nominal
        subtype, plus all component junk.

 11.b   Implicit_dereferences are covered by expression.

   12  [{freezing [type caused by a range]} At the place where a range
       causes freezing, the type of the range is frozen.]

 12.a   Proof:  This is consequence of the facts that expressions freeze
        their type, and the Range attribute is defined to be equivalent
        to a pair of expressions separated by ``..''.}

   13  {freezing [designated subtype caused by an allocator]} At the
       place where an allocator causes freezing, the designated subtype
       of its type is frozen.  If the type of the allocator is a derived
       type, then all ancestor types are also frozen.

 13.a   Ramification:  Allocators also freeze the named subtype, as a
        consequence of other rules.

 13.b   The ancestor types are frozen to prevent things like this:

13.c        type Pool_Ptr is access System.Storage_Pools.Root_Storage_Pool'Clas\
s;
            function F return Pool_Ptr;

13.d        package P is
                type A1 is access Boolean;
                type A2 is new A1;
                type A3 is new A2;
                X : A3 := new Boolean; -- Don't know what pool yet!
                for A1'Storage_Pool use F.all;
            end P;

 13.e   This is necessary because derived access types share their
        parent's pool.

   14  {freezing [subtypes of the profile of a callable entity]} At the
       place where a callable entity is frozen, each subtype of its
       profile is frozen.  If the callable entity is a member of an
       entry family, the index subtype of the family is frozen.
       {freezing [function call]} At the place where a function call
       causes freezing, if a parameter of the call is defaulted, the
       default_expression for that parameter causes freezing.

 14.a   Discussion:  We don't worry about freezing for procedure calls
        or entry calls, since a body freezes everything that precedes
        it, and the end of a declarative part freezes everything in the
        declarative part.

   15  {freezing [type caused by the freezing of a subtype]} At the
       place where a subtype is frozen, its type is frozen.  {freezing
       [constituents of a full type definition]} {freezing [first
       subtype caused by the freezing of the type]} At the place where a
       type is frozen, any expressions or names within the full type
       definition cause freezing; the first subtype, and any component
       subtypes, index subtypes, and parent subtype of the type are
       frozen as well.  {freezing [class-wide type caused by the
       freezing of the specific type]} {freezing [specific type caused
       by the freezing of the class-wide type]} For a specific tagged
       type, the corresponding class-wide type is frozen as well.  For a
       class-wide type, the corresponding specific type is frozen as
       well.

 15.a   Ramification:  Freezing a type needs to freeze its first subtype
        in order to preserve the property that the subtype-specific
        aspects of statically matching subtypes are the same.

 15.b   Freezing an access type does not freeze its designated subtype.


                               Legality Rules

16   [The explicit declaration of a primitive subprogram of a tagged type
shall occur before the type is frozen (see 3.9.2).]

        16.a   Reason:  This rule is needed because (1) we don't want people
        dispatching to things that haven't been declared yet, and (2) we want
        to allow tagged type descriptors to be static (allocated statically,
        and initialized to link-time-known symbols).  Suppose T2 inherits
        primitive P from T1, and then overrides P. Suppose P is called before
        the declaration of the overriding P. What should it dispatch to?  If
        the answer is the new P, we've violated the first principle above.
        If the answer is the old P, we've violated the second principle.  (A
        call to the new one necessarily raises Program_Error, but that's
        beside the point.)

        16.b   Note that a call upon a dispatching operation of type T will
        freeze T.

        16.c   We considered applying this rule to all derived types, for
        uniformity.  However, that would be upward incompatible, so we
        rejected the idea.  As in Ada 83, for an untagged type, the above
        call upon P will call the old P (which is arguably confusing).

17   [A type shall be completely defined before it is frozen (see 3.11.1 and
7.3).]

18   [The completion of a deferred constant declaration shall occur before
the constant is frozen (see 7.4).]

19   [A representation item that directly specifies an aspect of an entity
shall appear before the entity is frozen (see 13.1).]

        19.a   Change:  The above rules are now officially stated elsewhere,
        as per WG9 resolution, so the ones here are marked as [redundant].

        19.b   Discussion:  From RM83-13.1(7).  The wording here forbids
        freezing within the representation_clause itself, which was not true
        of the Ada 83 wording.  The wording of this rule is carefully written
        to work properly for type-related representation items.  For example,
        an enumeration_representation_clause is illegal after the type is
        frozen, even though the _clause refers to the first subtype.

        19.c   Proof:  The above Legality Rules are stated ``officially'' in
        the referenced clauses.

        19.d   Discussion:  Here's an example that illustrates when freezing
        occurs in the presence of defaults:

19.e        type T is ...;
            function F return T;
            type R is
                record
                    C : T := F;
                    D : Boolean := F = F;
                end record;
            X : R;

        19.f   Since the elaboration of R's declaration does not allocate
        component C, there is no need to freeze C's subtype at that place.
        Similarly, since the elaboration of R does not evaluate the default_
        expression ``F = F'', there is no need to freeze the types involved
        at that point.  However, the declaration of X does need to freeze
        these things.  Note that even if component C did not exist, the
        elaboration of the declaration of X would still need information
        about T -- even though D is not of type T, its default_expression
        requires that information.

        19.g   Ramification:  Although we define freezing in terms of the
        program text as a whole (i.e. after applying the rules of Section
        10), the freezing rules actually have no effect beyond compilation
        unit boundaries.

        19.h   Reason:  That is important, because Section 10 allows some
        implementation definedness in the order of things, and we don't want
        the freezing rules to be implementation defined.

        19.i   Ramification:  These rules also have no effect in statements
        -- they only apply within a single declarative_part, package_
        specification, task_definition, protected_definition, or protected_
        body.

        19.j   Implementation Note:  An implementation may choose to generate
        code for default_expressions and default_names in line at the place
        of use.  {thunk} Alternatively, an implementation may choose to
        generate thunks (subprograms implicitly generated by the compiler)
        for evaluation of defaults.  Thunk generation cannot, in general, be
        done at the place of the declaration that includes the default.
        Instead, they can be generated at the first freezing point of the
        type(s) involved.  (It is impossible to write a purely one-pass Ada
        compiler, for various reasons.  This is one of them -- the compiler
        needs to store a representation of defaults in its symbol table, and
        then walk that representation later, no earlier than the first
        freezing point.)

        19.k   In implementation terms, the linear elaboration model can be
        thought of as preventing uninitialized dope.  For example, the
        implementation might generate dope to contain the size of a private
        type.  This dope is initialized at the place where the type becomes
        completely defined.  It cannot be initialized earlier, because of the
        order-of-elaboration rules.  The freezing rules prevent elaboration
        of earlier declarations from accessing the size dope for a private
        type before it is initialized.

        19.l   2.8 overrides the freezing rules in the case of unrecognized
        pragmas.

        19.m   A representation_clause for an entity should most certainly
        not be a freezing point for the entity.


                        Incompatibilities With Ada 83

        19.n   {incompatibilities with Ada 83} RM83 defines a forcing
        occurrence of a type as follows:  ``A forcing occurrence is any
        occurrence [of the name of the type, subtypes of the type, or types
        or subtypes with subcomponents of the type] other than in a type or
        subtype declaration, a subprogram specification, an entry
        declaration, a deferred constant declaration, a pragma, or a
        representation_clause for the type itself. In any case, an occurrence
        within an expression is always forcing.''

        19.o   It seems like the wording allows things like this:

19.p        type A is array(Integer range 1..10) of Boolean;
            subtype S is Integer range A'Range;
                -- not forcing for A

        19.q   Occurrences within pragmas can cause freezing in Ada 9X.
        (Since such pragmas are ignored in Ada 83, this will probably fix
        more bugs than it causes.)

                            Extensions to Ada 83

        19.r   {extensions to Ada 83} In Ada 9X, generic_formal_parameter_
        declarations do not normally freeze the entities from which they are
        defined.  For example:

19.s        package Outer is
                type T is tagged limited private;
                generic
                    type T2 is
                        new T with private; -- Does not freeze T
                                            -- in Ada 9X.
                package Inner is
                    ...
                end Inner;
            private
                type T is ...;
            end Outer;

        19.t   This is important for the usability of generics.  The above
        example uses the Ada 9X feature of formal derived types.  Examples
        using the kinds of formal parameters already allowed in Ada 83 are
        well known.  See, for example, comments 83-00627 and 83-00688.  The
        extensive use expected for formal derived types makes this issue even
        more compelling than described by those comments.  Unfortunately, we
        are unable to solve the problem that explicit_generic_actual_
        parameters cause freezing, even though a package equivalent to the
        instance would not cause freezing.  This is primarily because such an
        equivalent package would have its body in the body of the containing
        program unit, whereas an instance has its body right there.

                         Wording Changes From Ada 83

        19.u   The concept of freezing is based on Ada 83's concept of
        ``forcing occurrences.''  The first freezing point of an entity
        corresponds roughly to the place of the first forcing occurrence, in
        Ada 83 terms.  The reason for changing the terminology is that the
        new rules do not refer to any particular ``occurrence'' of a name of
        an entity.  Instead, we refer to ``uses'' of an entity, which are
        sometimes implicit.

        19.v   In Ada 83, forcing occurrences were used only in rules about
        representation_clauses.  We have expanded the concept to cover
        private types, because the rules stated in RM83-7.4.1(4) are almost
        identical to the forcing occurrence rules.

        19.w   The Ada 83 rules are changed in Ada 9X for the following
        reasons:

         19.x  The Ada 83 rules do not work right for subtype-specific
               aspects.  In an earlier version of Ada 9X, we considered
               allowing representation items to apply to subtypes other
               than the first subtype.  This was part of the reason for
               changing the Ada 83 rules.  However, now that we have
               dropped that functionality, we still need the rules to be
               different from the Ada 83 rules.

         19.y  The Ada 83 rules do not achieve the intended effect.  In
               Ada 83, either with or without the AIs, it is possible to
               force the compiler to generate code that references
               uninitialized dope, or force it to detect erroneousness
               and exception raising at compile time.

         19.z  It was a goal of Ada 83 to avoid uninitialized access
               values.  However, in the case of deferred constants, this
               goal was not achieved.

         19.aa  The Ada 83 rules are not only too weak -- they are also
               too strong.  They allow loopholes (as described above),
               but they also prevent certain kinds of default_
               expressions that are harmless, and certain kinds of
               generic_declarations that are both harmless and very
               useful.

         19.bb  Ada 83 had a case where a representation_clause had a
               strong effect on the semantics of the program -- 'Small.
               This caused certain semantic anomalies.  There are more
               cases in Ada 9X, because the attribute_representation_
               clause has been generalized.



















                           THE STANDARD LIBRARIES



                                   Annex A
                                 (normative)


                       Predefined Language Environment



1   [{Language-Defined Library Units} {predefined environment} This Annex
contains the specifications of library units that shall be provided by every
implementation.  There are three root library units:  Ada, Interfaces, and
System; other library units are children of these:

2   Standard -- A.1
      Ada -- A.2
         Asynchronous_Task_Control -- D.11
         Calendar -- 9.6
         Characters -- A.3.1
            Handling -- A.3.2
            Latin_1 -- A.3.3
         Command_Line -- A.15
         Decimal -- F.2
         Direct_IO -- A.8.4
         Dynamic_Priorities -- D.5
         Exceptions -- 11.4.1
         Finalization -- 7.6
         Interrupts -- C.3.2
            Names -- C.3.2
         IO_Exceptions -- A.13
         Numerics -- A.5
            Complex_Elementary_Functions -- G.1.2
            Complex_Types -- G.1.1
            Discrete_Random -- A.5.2
            Elementary_Functions -- A.5.1
            Float_Random -- A.5.2
            Generic_Complex_Elementary_Functions -- G.1.2
            Generic_Complex_Types -- G.1.1
            Generic_Elementary_Functions -- A.5.1
         Real_Time -- D.8
         Sequential_IO -- A.8.1
         Storage_IO -- A.9
         Streams -- 13.13.1
            Stream_IO -- A.12.1
         Strings -- A.4.1
            Bounded -- A.4.4
            Fixed -- A.4.3
            Maps -- A.4.2
               Constants -- A.4.6
            Unbounded -- A.4.5
            Wide_Bounded -- A.4.7
            Wide_Fixed -- A.4.7
            Wide_Maps -- A.4.7
               Wide_Constants -- A.4.7
            Wide_Unbounded -- A.4.7
    Standard (...continued)
      Ada (...continued)
         Synchronous_Task_Control -- D.10
         Tags -- 3.9
         Task_Attributes -- C.7.2
         Task_Identification -- C.7.1
         Text_IO -- A.10.1
            Complex_IO -- G.1.3
            Editing -- F.3.3
            Text_Streams -- A.12.2
         Unchecked_Conversion -- 13.9
         Unchecked_Deallocation -- 13.11.2
         Wide_Text_IO -- A.11
            Complex_IO -- G.1.3
            Editing -- F.3.4
            Text_Streams -- A.12.3

      Interfaces -- B.2
         C -- B.3
            Pointers -- B.3.2
            Strings -- B.3.1
         COBOL -- B.4
         Fortran -- B.5

      System -- 13.7
         Address_To_Access_Conversions -- 13.7.2
         Machine_Code -- 13.8
         RPC -- E.5
         Storage_Elements -- 13.7.1
         Storage_Pools -- 13.11

]

        2.a   Discussion:  In running text, we generally leave out the
        ``Ada.'' when referring to a child of Ada.

        2.b   Reason:  We had no strict rule for which of Ada, Interfaces, or
        System should be the parent of a given library unit.  However, we
        have tried to place as many things as possible under Ada, except that
        interfacing is a separate category, and we have tried to place
        library units whose use is highly non-portable under System.


                         Implementation Requirements

3   The implementation shall ensure that each language defined subprogram is
reentrant in the sense that concurrent calls on the same subprogram perform
as specified, so long as all parameters that could be passed by reference
denote nonoverlapping objects.

        3.a   Ramification:  For example, simultaneous calls to Text_IO.Put
        will work properly, so long as they are going to two different files.
        On the other hand, simultaneous output to the same file constitutes
        erroneous use of shared variables.

        3.b   To be honest:  Here, ``language defined subprogram'' means a
        language defined library subprogram, a subprogram declared in the
        visible part of a language defined library package, an instance of a
        language defined generic library subprogram, or a subprogram declared
        in the visible part of an instance of a language defined generic
        library package.

        3.c   Ramification:  The rule implies that any data local to the
        private part or body of the package has to be somehow protected
        against simultaneous access.


                         Implementation Permissions

4   The implementation may restrict the replacement of language-defined
compilation units.  The implementation may restrict children of
language-defined library units (other than Standard).

        4.a   Ramification:  For example, the implementation may say, ``you
        cannot compile a library unit called System'' or ``you cannot compile
        a child of package System'' or ``if you compile a library unit called
        System, it has to be a package, and it has to contain at least the
        following declarations: ...''.


                         Wording Changes From Ada 83

        4.b   Many of Ada 83's language-defined library units are now
        children of Ada or System.  For upward compatibility, these are
        renamed as root library units (see J.1).

        4.c   The order and lettering of the annexes has been changed.



A.1 The Package Standard

1   This clause outlines the specification of the package Standard containing
all predefined identifiers in the language.  {unspecified [partial]} The
corresponding package body is not specified by the language.

2   The operators that are predefined for the types declared in the package
Standard are given in comments since they are implicitly declared.  {italics
(pseudo-names of anonymous types)} Italics are used for pseudo-names of
anonymous types (such as root_real) and for undefined information (such as
implementation-defined).

        2.a   Ramification:  All of the predefined operators are of
        convention Intrinsic.


                              Static Semantics

3   The library package Standard has the following declaration:

        3.a   Implementation defined:  The names and characteristics of the
        numeric subtypes declared in the visible part of package Standard.

4   package Standard is
       pragma Pure(Standard);

5      type Boolean is (False, True);

6      -- The predefined relational operators for this type are as follows:

7      -- function "="   (Left, Right : Boolean) return Boolean;
       -- function "/="  (Left, Right : Boolean) return Boolean;
       -- function "<"   (Left, Right : Boolean) return Boolean;
       -- function "<="  (Left, Right : Boolean) return Boolean;
       -- function ">"   (Left, Right : Boolean) return Boolean;
       -- function ">="  (Left, Right : Boolean) return Boolean;

8      -- The predefined logical operators and the predefined logical
       -- negation operator are as follows:

9      -- function "and" (Left, Right : Boolean) return Boolean;
       -- function "or"  (Left, Right : Boolean) return Boolean;
       -- function "xor" (Left, Right : Boolean) return Boolean;

10     -- function "not" (Right : Boolean) return Boolean;

11     -- The integer type root_integer is predefined.
       -- The corresponding universal type is universal_integer.

12     type Integer is range implementation-defined;

13     subtype Natural  is Integer range 0 .. Integer'Last;
       subtype Positive is Integer range 1 .. Integer'Last;

14     -- The predefined operators for type Integer are as follows:

15     -- function "="  (Left, Right : Integer'Base) return Boolean;
       -- function "/=" (Left, Right : Integer'Base) return Boolean;
       -- function "<"  (Left, Right : Integer'Base) return Boolean;
       -- function "<=" (Left, Right : Integer'Base) return Boolean;
       -- function ">"  (Left, Right : Integer'Base) return Boolean;
       -- function ">=" (Left, Right : Integer'Base) return Boolean;

16     -- function "+"   (Right : Integer'Base) return Integer'Base;
       -- function "-"   (Right : Integer'Base) return Integer'Base;
       -- function "abs" (Right : Integer'Base) return Integer'Base;

17     -- function "+"   (Left, Right : Integer'Base) return Integer'Base;
       -- function "-"   (Left, Right : Integer'Base) return Integer'Base;
       -- function "*"   (Left, Right : Integer'Base) return Integer'Base;
       -- function "/"   (Left, Right : Integer'Base) return Integer'Base;
       -- function "rem" (Left, Right : Integer'Base) return Integer'Base;
       -- function "mod" (Left, Right : Integer'Base) return Integer'Base;

18     -- function "**"  (Left : Integer'Base; Right : Natural) return Integer'\
Base;

19     -- The specification of each operator for the type
       -- root_integer, or for any additional predefined integer
       -- type, is obtained by replacing Integer by the name of the type
       -- in the specification of the corresponding operator of the type
       -- Integer.  The right operand of the exponentiation operator{94-4693.v}
       -- remains as subtype Natural.

20     -- The floating point type root_real is predefined.
       -- The corresponding universal type is universal_real.

21     type Float is digits implementation-defined;

22     -- The predefined operators for this type are as follows:

23     -- function "="   (Left, Right : Float) return Boolean;
       -- function "/="  (Left, Right : Float) return Boolean;
       -- function "<"   (Left, Right : Float) return Boolean;
       -- function "<="  (Left, Right : Float) return Boolean;
       -- function ">"   (Left, Right : Float) return Boolean;
       -- function ">="  (Left, Right : Float) return Boolean;

24     -- function "+"   (Right : Float) return Float;
       -- function "-"   (Right : Float) return Float;
       -- function "abs" (Right : Float) return Float;

25     -- function "+"   (Left, Right : Float) return Float;
       -- function "-"   (Left, Right : Float) return Float;
       -- function "*"   (Left, Right : Float) return Float;
       -- function "/"   (Left, Right : Float) return Float;

26     -- function "**"  (Left : Float; Right : Integer'Base) return Float;

27     -- The specification of each operator for the type  root_real,  or  for
       -- any  additional  predefined  floating  point  type,  is  obtained  by
       -- replacing  Float by the name of  the type in the specification of the
       -- corresponding  operator  of  the  type  Float.

28     -- In  addition,  the  following operators are predefined for the root
       -- numeric types:

29     function "*" (Left : root_integer; Right : root_real)
         return root_real;

30     function "*" (Left : root_real;    Right : root_integer)
         return root_real;

31     function "/" (Left : root_real;    Right : root_integer)
         return root_real;

32     -- The type universal_fixed is predefined.
       -- The only multiplying operators defined between
       -- fixed point types are

33     function "*" (Left : universal_fixed; Right : universal_fixed)
         return universal_fixed;

34     function "/" (Left : universal_fixed; Right : universal_fixed)
         return universal_fixed;


          -- The declaration of type Character is based on the standard ISO 885\
9-1 character set.

35        -- There are no character literals corresponding to the positions for\
 control characters.
          -- They are indicated in italics in this definition.  See 3.5.2.

       type Character is

         (nul,  soh,  stx,  etx,     eot,  enq,  ack,  bel,
          bs,   ht,   lf,   vt,      ff,   cr,   so,   si,

          dle,  dc1,  dc2,  dc3,     dc4,  nak,  syn,  etb,
          can,  em,   sub,  esc,     fs,   gs,   rs,   us,

          ' ',  '!',  '"',  '#',     '$',  '%',  '&',  ''',
          '(',  ')',  '*',  '+',     ',',  '-',  '.',  '/',

          '0',  '1',  '2',  '3',     '4',  '5',  '6',  '7',
          '8',  '9',  ':',  ';',     '<',  '=',  '>',  '?',

          '@',  'A',  'B',  'C',     'D',  'E',  'F',  'G',
          'H',  'I',  'J',  'K',     'L',  'M',  'N',  'O',

          'P',  'Q',  'R',  'S',     'T',  'U',  'V',  'W',
          'X',  'Y',  'Z',  '[',     '\',  ']',  '^',  '_',

          '`',  'a',  'b',  'c',     'd',  'e',  'f',  'g',
          'h',  'i',  'j',  'k',     'l',  'm',  'n',  'o',

          'p',  'q',  'r',  's',     't',  'u',  'v',  'w',
          'x',  'y',  'z',  '{',     '|',  '}',  '~',  del,


          reserved_128,     reserved_129,  bph,  nbh,
          reserved_132,     nel,     ssa,  esa,

          hts,  htj,  vts,  pld,     plu,  ri,   ss2,  ss3,

          dcs,  pu1,  pu2,  sts,     cch,  mw,   spa,  epa,

          sos, reserved_153, sci, csi,
          st,   osc,  pm,   apc,


    ... );

36     -- The predefined operators for the type Character are the  same  as  for
       -- any enumeration type.


       -- The declaration of type Wide_Character is based on the standard ISO 1\
0646 BMP character set.
       -- The first 256 positions have the same contents as type Character.  Se\
e 3.5.2.

       type Wide_Character is (nul, soh ... FFFE, FFFF);


       package ASCII is ... end ASCII;  --Obsolescent; see J.5
    {ASCII (package physically nested within the declaration of Standard)}


       -- Predefined string types:

37     type String is array(Positive range <>) of Character;
       pragma Pack(String);

38     -- The predefined operators for this type are as follows:

39     --     function "="  (Left, Right: String) return Boolean;
       --     function "/=" (Left, Right: String) return Boolean;
       --     function "<"  (Left, Right: String) return Boolean;
       --     function "<=" (Left, Right: String) return Boolean;
       --     function ">"  (Left, Right: String) return Boolean;
       --     function ">=" (Left, Right: String) return Boolean;

40     --     function "&" (Left: String;    Right: String)    return String;
       --     function "&" (Left: Character; Right: String)    return String;
       --     function "&" (Left: String;    Right: Character) return String;
       --     function "&" (Left: Character; Right: Character) return String;

41     type Wide_String is array(Positive range <>) of Wide_Character;
       pragma Pack(Wide_String);

42     -- The predefined operators for this type correspond to those for String

43     type Duration is delta implementation-defined range implementation-defin\
ed;

44        -- The  predefined  operators for the type Duration are the same as f\
or
          -- any fixed point type.

45     -- The predefined exceptions:

46     Constraint_Error: exception;
       Program_Error   : exception;
       Storage_Error   : exception;
       Tasking_Error   : exception;

47  end Standard;

{94-4487.a} {94-4704.a} {94-4510.a} {94-4709.a}

48   Standard has no private part.

        48.a   Reason:  This is important for portability.  All library
        packages are children of Standard, and if Standard had a private part
        then it would be visible to all of them.

49   In each of the types Character and Wide_Character, the character
literals for the space character (position 32) and the non-breaking space
character (position 160) correspond to different values. Unless indicated
otherwise, each occurrence of the character literal ' ' in this International
Standard refers to the space character.  Similarly, the character literals
for hyphen (position 45) and soft hyphen (position 173) correspond to
different values.  Unless indicated otherwise, each occurrence of the
character literal '-' in this International Standard refers to the hyphen
character.


                              Dynamic Semantics

50   {elaboration [package_body of Standard]} Elaboration of the body of
Standard has no effect.

        50.a   Discussion:  Note that the language does not define where this
        body appears in the environment declarative_part -- see Section 10,
        ``Program Structure and Compilation Issues''.


                         Implementation Permissions

51   An implementation may provide additional predefined integer types and
additional predefined floating point types.  Not all of these types need have
names.

        51.a   To be honest:  An implementation may add representation items
        to package Standard, for example to specify the internal codes of
        type Boolean, or the Small of type Duration.  {94-4693.i}


                            Implementation Advice

52   If an implementation provides additional named predefined integer types,
then the names should end with ``Integer'' as in ``Long_Integer''.  If an
implementation provides additional named predefined floating point types,
then the names should end with ``Float'' as in ``Long_Float''.


     NOTES
53   (1) Certain aspects of the predefined entities cannot be completely
     described in the language itself.  For example, although the enumeration
     type Boolean can be written showing the two enumeration literals False
     and True, the short-circuit control forms cannot be expressed in the
     language.

54   (2) As explained in 8.1, ``Declarative Region'' and 10.1.4, ``The
     Compilation Process'', the declarative region of the package Standard
     encloses every library unit and consequently the main subprogram; the
     declaration of every library unit is assumed to occur within this
     declarative region.  Library_items are assumed to be ordered in such a
     way that there are no forward semantic dependences.  However, as
     explained in 8.3, ``Visibility'', the only library units that are
     visible within a given compilation unit are the library units named by
     all with_clauses that apply to the given unit, and moreover, within the
     declarative region of a given library unit, that library unit itself.

55   (3) If all block_statements of a program are named, then the name of
     each program unit can always be written as an expanded name starting
     with Standard (unless Standard is itself hidden).  The name of a library
     unit cannot be a homograph of a name (such as Integer) that is already
     declared in Standard.

56   (4) The exception Standard.Numeric_Error is defined in J.6.

   56.a   Discussion:  The declaration of Natural needs to appear between the
        declaration of Integer and the (implicit) declaration of the "**"
        operator for Integer, because a formal parameter of "**" is of
        subtype Natural.  This would be impossible in normal code, because
        the implicit declarations for a type occur immediately after the type
        declaration, with no possibility of intervening explicit declara-
        tions.  But we're in Standard, and Standard is somewhat magic anyway.

   56.b   Using Natural as the subtype of the formal of "**" seems natural;
        it would be silly to have a textual rule about Constraint_Error being
        raised when there is a perfectly good subtype that means just that.
        Furthermore, by not using Integer for that formal, it helps remind
        the reader that the exponent remains Natural even when the left
        operand is replaced with the derivative of Integer.  It doesn't
        logically imply that, but it's still useful as a reminder.

   56.c   In any case, declaring these general-purpose subtypes of Integer
        close to Integer seems more readable than declaring them much later.


                            Extensions to Ada 83

        56.d   {extensions to Ada 83} Package Standard is declared to be
        pure.

        56.e   Discussion:  The introduction of the types Wide_Character and
        Wide_String is not an Ada 9X extension to Ada 83, since ISO WG9 has
        approved these as an authorized extension of the original Ada 83
        standard that is part of that standard.

                         Wording Changes From Ada 83

        56.f   Numeric_Error is made obsolescent.

        56.g   The declarations of Natural and Positive are moved to just
        after the declaration of Integer, so that "**" can refer to Natural
        without a forward reference.  There's no real need to move Positive,
        too -- it just came along for the ride.



A.2 The Package Ada

                              Static Semantics

1   The following language-defined library package exists:

2   package Ada is
        pragma Pure(Ada);
    end Ada;

3   Ada serves as the parent of most of the other language-defined library
units; its declaration is empty (except for the pragma Pure).


                               Legality Rules

4   In the standard mode, it is illegal to compile a child of package Ada.

        4.a   Reason:  The intention is that mentioning, say, Ada.Text_IO in
        a with_clause is guaranteed (at least in the standard mode) to refer
        to the standard version of Ada.Text_IO.  The user can compile a root
        library unit Text_IO that has no relation to the standard version of
        Text_IO.

        4.b   Ramification:  Note that Ada can have non-language-defined
        grandchildren, assuming the implementation allows it.  Also, packages
        System and Interfaces can have children, assuming the implementation
        allows it.

        4.c   Implementation Note:  An implementation will typically support
        a nonstandard mode in which compiling the language defined library
        units is allowed.  Whether or not this mode is made available to
        users is up to the implementer.

        4.d   An implementation could theoretically have private children of
        Ada, since that would be semantically neutral.  However, a programmer
        cannot compile such a library unit.


                            Extensions to Ada 83

        4.e   {extensions to Ada 83} This clause is new to Ada 9X.



A.3 Character Handling

1   This clause presents the packages related to character processing:  an
empty pure package Characters and child packages Characters.Handling and
Characters.Latin_1.  The package Characters.Handling provides classification
and conversion functions for Character data, and some simple functions for
dealing with Wide_Character data.  The child package Characters.Latin_1
declares a set of constants initialized to values of type Character.


                            Extensions to Ada 83

        1.a   {extensions to Ada 83} This clause is new to Ada 9X.



A.3.1 The Package Characters

                              Static Semantics

1   The library package Characters has the following declaration:

2   package Ada.Characters is
      pragma Pure(Characters);
    end Ada.Characters;



A.3.2 The Package Characters.Handling

                              Static Semantics

1   The library package Characters.Handling has the following declaration:

2   package Ada.Characters.Handling is
      pragma Preelaborate(Handling);

3   --Character classification functions

4     function Is_Control           (Item : in Character) return Boolean;
      function Is_Graphic           (Item : in Character) return Boolean;
      function Is_Letter            (Item : in Character) return Boolean;
      function Is_Lower             (Item : in Character) return Boolean;
      function Is_Upper             (Item : in Character) return Boolean;
      function Is_Basic             (Item : in Character) return Boolean;
      function Is_Digit             (Item : in Character) return Boolean;
      function Is_Decimal_Digit     (Item : in Character) return Boolean rename\
s Is_Digit;
      function Is_Hexadecimal_Digit (Item : in Character) return Boolean;
      function Is_Alphanumeric      (Item : in Character) return Boolean;
      function Is_Special           (Item : in Character) return Boolean;

5   --Conversion functions for Character and String

6     function To_Lower (Item : in Character) return Character;
      function To_Upper (Item : in Character) return Character;
      function To_Basic (Item : in Character) return Character;

7     function To_Lower (Item : in String) return String;
      function To_Upper (Item : in String) return String;
      function To_Basic (Item : in String) return String;

8   --Classifications of and conversions between Character and ISO 646

9     subtype ISO_646 is
        Character range Character'Val(0) .. Character'Val(127);

10    function Is_ISO_646 (Item : in Character) return Boolean;
      function Is_ISO_646 (Item : in String)    return Boolean;

11    function To_ISO_646 (Item       : in Character;
                           Substitute : in ISO_646 := ' ')
        return ISO_646;

12    function To_ISO_646 (Item       : in String;
                           Substitute : in ISO_646 := ' ')
        return String;

13  --Classifications of and conversions between Wide_Character and Character.

14    function Is_Character (Item : in Wide_Character) return Boolean;
      function Is_String    (Item : in Wide_String)    return Boolean;

15    function To_Character (Item       : in Wide_Character;
                             Substitute : in Character := ' ')
        return Character;

16    function To_String    (Item       : in Wide_String;
                             Substitute : in Character := ' ')
        return String;

17    function To_Wide_Character (Item : in Character) return Wide_Character;

18    function To_Wide_String    (Item : in String)    return Wide_String;

19  end Ada.Characters.Handling;

{94-4469.a} {94-4884.a}

20   In the description below for each function that returns a Boolean
result, the effect is described in terms of the conditions under which the
value True is returned.  If these conditions are not met, then the function
returns False.

21   Each of the following classification functions has a formal Character
parameter, Item, and returns a Boolean result.

22  {control character (a category of Character)} Is_Control
                True if Item is a control character.  A control character is
                a character whose position is in one of the ranges 0..31 or
                127..159.

23  {graphic character (a category of Character)} Is_Graphic
                True if Item is a graphic character.  A graphic character is
                a character whose position is in one of the ranges 32..126 or
                160..255.

24  {letter (a category of Character)} Is_Letter
                True if Item is a letter.  A letter is a character that is in
                one of the ranges 'A'..'Z' or 'a'..'z', or whose position is
                in one of the ranges 192..214, 216..246, or 248..255.

25  {lower-case letter (a category of Character)} Is_Lower
                True if Item is a lower-case letter.  A lower-case letter is
                a character that is in the range 'a'..'z', or whose position
                is in one of the ranges 223..246 or 248..255.

26  {upper-case letter (a category of Character)} Is_Upper
                True if Item is an upper-case letter.  An upper-case letter
                is a character that is in the range 'A'..'Z' or whose
                position is in one of the ranges 192..214 or 216.. 222.

27  {basic letter (a category of Character)} Is_Basic
                True if Item is a basic letter.  A basic letter is a
                character that is in one of the ranges 'A'..'Z' and 'a'..'z',
                or that is one of the following:  an upper- or lower-case AE
                diphthong, an upper- or lower-case Icelandic eth, an upper-
                or lower-case Icelandic thorn, or a sharp-s.

28  {decimal digit (a category of Character)} Is_Digit
                True if Item is a decimal digit.  A decimal digit is a
                character in the range '0'..'9'.

29  Is_Decimal_Digit
                A renaming of Is_Digit.

30  {hexadecimal digit (a category of Character)} Is_Hexadecimal_
                Digit
                True if Item is a hexadecimal digit.  A hexadecimal digit is
                a character that is either a decimal digit or that is in one
                of the ranges 'A' .. 'F' or 'a' .. 'f'.

31  {alphanumeric character (a category of Character)} Is_
                Alphanumeric
                True if Item is an alphanumeric character.  An alphanumeric
                character is a character that is either a letter or a decimal
                digit.

32  {special graphic character (a category of Character)} Is_
                Special
                True if Item is a special graphic character.  A special
                graphic character is a graphic character that is not
                alphanumeric.

33   Each of the names To_Lower, To_Upper, and To_Basic refers to two
functions: one that converts from Character to Character, and the other that
converts from String to String.  The result of each Character-to-Character
function is described below, in terms of the conversion applied to Item, its
formal Character parameter.  The result of each String-to-String conversion
is obtained by applying to each element of the function's String parameter
the corresponding Character-to-Character conversion; the result is the null
String if the value of the formal parameter is the null String.  The lower
bound of the result String is 1.

34  To_Lower
                Returns the corresponding lower-case value for Item if Is_
                Upper(Item), and returns Item otherwise.

35  To_Upper
                Returns the corresponding upper-case value for Item if Is_
                Lower(Item) and Item has an upper-case form, and returns Item
                otherwise.  The lower case letters sharp-s and y-diaeresis do
                not have upper case forms.

36  To_Basic
                Returns the letter corresponding to Item but with no
                diacritical mark, if Item is a letter but not a basic letter;
                returns Item otherwise.

37   The following set of functions test for membership in the ISO 646
character range, or convert between ISO 646 and Character.

38  Is_ISO_646
                The function whose formal parameter, Item, is of type
                Character returns True if Item is in the subtype ISO_646.

39  Is_ISO_646
                The function whose formal parameter, Item, is of type String
                returns True if Is_ISO_646(Item(I)) is True for each I in
                Item'Range.

40  To_ISO_646
                The function whose first formal parameter, Item, is of type
                Character returns Item if Is_ISO_646(Item), and returns the
                Substitute ISO_646 character otherwise.

41  To_ISO_646
                The function whose first formal parameter, Item, is of type
                String returns the String whose Range is 1..Item'Length and
                each of whose elements is given by To_ISO_646 of the
                corresponding element in Item.

42   The following set of functions test Wide_Character values for membership
in Character, or convert between corresponding characters of Wide_Character
and Character.  {94-4913.a}

43  Is_Character
                Returns True if Wide_Character'Pos(Item) <=
                Character'Pos(Character'Last).

44  Is_String
                Returns True if Is_Character(Item(I)) is True for each I in
                Item'Range.

45  To_Character
                Returns the Character corresponding to Item if Is_
                Character(Item), and returns the Substitute Character
                otherwise.

46  To_String
                Returns the String whose range is 1..Item'Length and each of
                whose elements is given by To_Character of the corresponding
                element in Item.

47  To_Wide_Character
                Returns the Wide_Character X such that Character'Pos(Item) =
                Wide_Character'Pos(X).

48  To_Wide_String
                Returns the Wide_String whose range is 1..Item'Length and
                each of whose elements is given by To_Wide_Character of the
                corresponding element in Item.


                            Implementation Advice

49   If an implementation provides a localized definition of Character or
Wide_Character, then the effects of the subprograms in Characters.Handling
should reflect the localizations.  See also 3.5.2.


     NOTES
50   (5) A basic letter is a letter without a diacritical mark.

51   (6) Except for the hexadecimal digits, basic letters, and ISO_646
     characters, the categories identified in the classification functions
     form a strict hierarchy:

        52  Control characters

        53  Graphic characters

               54  Alphanumeric characters

                      55  Letters

                             56  Upper-case letters

                             57  Lower-case letters

                      58  Decimal digits

               59  Special graphic characters

   59.a   Ramification:  Thus each Character value is either a control
        character or a graphic character but not both; each graphic character
        is either an alphanumeric or special graphic but not both; each
        alphanumeric is either a letter or decimal digit but not both; each
        letter is either upper case or lower case but not both.



A.3.3 The Package Characters.Latin_1

1   The package Characters.Latin_1 declares constants for characters in ISO
8859-1.

        1.a   Reason:  The constants for the ISO 646 characters could have
        been declared as renamings of objects declared in package ASCII, as
        opposed to explicit constants.  The main reason for explicit
        constants was for consistency of style with the upper-half constants,
        and to avoid emphasizing the package ASCII.


                              Static Semantics

2   The library package Characters.Latin_1 has the following declaration:

3   package Ada.Characters.Latin_1 is
        pragma Pure(Latin_1);

4   -- Control characters:{control character [a category of Character]}

5       NUL                  : constant Character := Character'Val(0);
        SOH                  : constant Character := Character'Val(1);
        STX                  : constant Character := Character'Val(2);
        ETX                  : constant Character := Character'Val(3);
        EOT                  : constant Character := Character'Val(4);
        ENQ                  : constant Character := Character'Val(5);
        ACK                  : constant Character := Character'Val(6);
        BEL                  : constant Character := Character'Val(7);
        BS                   : constant Character := Character'Val(8);
        HT                   : constant Character := Character'Val(9);
        LF                   : constant Character := Character'Val(10);
        VT                   : constant Character := Character'Val(11);
        FF                   : constant Character := Character'Val(12);
        CR                   : constant Character := Character'Val(13);
        SO                   : constant Character := Character'Val(14);
        SI                   : constant Character := Character'Val(15);

6       DLE                  : constant Character := Character'Val(16);
        DC1                  : constant Character := Character'Val(17);
        DC2                  : constant Character := Character'Val(18);
        DC3                  : constant Character := Character'Val(19);
        DC4                  : constant Character := Character'Val(20);
        NAK                  : constant Character := Character'Val(21);
        SYN                  : constant Character := Character'Val(22);
        ETB                  : constant Character := Character'Val(23);
        CAN                  : constant Character := Character'Val(24);
        EM                   : constant Character := Character'Val(25);
        SUB                  : constant Character := Character'Val(26);
        ESC                  : constant Character := Character'Val(27);
        FS                   : constant Character := Character'Val(28);
        GS                   : constant Character := Character'Val(29);
        RS                   : constant Character := Character'Val(30);
        US                   : constant Character := Character'Val(31);

7   -- ISO 646 graphic characters:

8       Space                : constant Character := ' ';  -- Character'Val(32)
        Exclamation          : constant Character := '!';  -- Character'Val(33)
        Quotation            : constant Character := '"';  -- Character'Val(34)
        Number_Sign          : constant Character := '#';  -- Character'Val(35)
        Dollar_Sign          : constant Character := '$';  -- Character'Val(36)
        Percent_Sign         : constant Character := '%';  -- Character'Val(37)
        Ampersand            : constant Character := '&';  -- Character'Val(38)
        Apostrophe           : constant Character := ''';  -- Character'Val(39)
        Left_Parenthesis     : constant Character := '(';  -- Character'Val(40)
        Right_Parenthesis    : constant Character := ')';  -- Character'Val(41)
        Asterisk             : constant Character := '*';  -- Character'Val(42)
        Plus_Sign            : constant Character := '+';  -- Character'Val(43)
        Comma                : constant Character := ',';  -- Character'Val(44)
        Hyphen               : constant Character := '-';  -- Character'Val(45)
        Minus_Sign           : Character renames Hyphen;
        Full_Stop            : constant Character := '.';  -- Character'Val(46)
        Solidus              : constant Character := '/';  -- Character'Val(47)

9       -- Decimal digits '0' though '9' are at positions 48 through 57

10      Colon                : constant Character := ':';  -- Character'Val(58)
        Semicolon            : constant Character := ';';  -- Character'Val(59)
        Less_Than_Sign       : constant Character := '<';  -- Character'Val(60)
        Equals_Sign          : constant Character := '=';  -- Character'Val(61)
        Greater_Than_Sign    : constant Character := '>';  -- Character'Val(62)
        Question             : constant Character := '?';  -- Character'Val(63)
        Commercial_At        : constant Character := '@';  -- Character'Val(64)

11      -- Letters 'A' through 'Z' are at positions 65 through 90

12      Left_Square_Bracket  : constant Character := '[';  -- Character'Val(91)
        Reverse_Solidus      : constant Character := '\';  -- Character'Val(92)
        Right_Square_Bracket : constant Character := ']';  -- Character'Val(93)
        Circumflex           : constant Character := '^';  -- Character'Val(94)
        Low_Line             : constant Character := '_';  -- Character'Val(95)

13      Grave                : constant Character := '`';  -- Character'Val(96)
        LC_A                 : constant Character := 'a';  -- Character'Val(97)
        LC_B                 : constant Character := 'b';  -- Character'Val(98)
        LC_C                 : constant Character := 'c';  -- Character'Val(99)
        LC_D                 : constant Character := 'd';  -- Character'Val(100)
        LC_E                 : constant Character := 'e';  -- Character'Val(101)
        LC_F                 : constant Character := 'f';  -- Character'Val(102)
        LC_G                 : constant Character := 'g';  -- Character'Val(103)
        LC_H                 : constant Character := 'h';  -- Character'Val(104)
        LC_I                 : constant Character := 'i';  -- Character'Val(105)
        LC_J                 : constant Character := 'j';  -- Character'Val(106)
        LC_K                 : constant Character := 'k';  -- Character'Val(107)
        LC_L                 : constant Character := 'l';  -- Character'Val(108)
        LC_M                 : constant Character := 'm';  -- Character'Val(109)
        LC_N                 : constant Character := 'n';  -- Character'Val(110)
        LC_O                 : constant Character := 'o';  -- Character'Val(111)

14      LC_P                 : constant Character := 'p';  -- Character'Val(112)
        LC_Q                 : constant Character := 'q';  -- Character'Val(113)
        LC_R                 : constant Character := 'r';  -- Character'Val(114)
        LC_S                 : constant Character := 's';  -- Character'Val(115)
        LC_T                 : constant Character := 't';  -- Character'Val(116)
        LC_U                 : constant Character := 'u';  -- Character'Val(117)
        LC_V                 : constant Character := 'v';  -- Character'Val(118)
        LC_W                 : constant Character := 'w';  -- Character'Val(119)
        LC_X                 : constant Character := 'x';  -- Character'Val(120)
        LC_Y                 : constant Character := 'y';  -- Character'Val(121)
        LC_Z                 : constant Character := 'z';  -- Character'Val(122)
        Left_Curly_Bracket   : constant Character := '{';  -- Character'Val(123)
        Vertical_Line        : constant Character := '|';  -- Character'Val(124)
        Right_Curly_Bracket  : constant Character := '}';  -- Character'Val(125)
        Tilde                : constant Character := '~';  -- Character'Val(126)
        DEL                  : constant Character := Character'Val(127);

15  -- ISO 6429 control characters:{control character [a category of Character]}

16      IS4                  : Character renames FS;
        IS3                  : Character renames GS;
        IS2                  : Character renames RS;
        IS1                  : Character renames US;

17      Reserved_128         : constant Character := Character'Val(128);
        Reserved_129         : constant Character := Character'Val(129);
        BPH                  : constant Character := Character'Val(130);
        NBH                  : constant Character := Character'Val(131);
        Reserved_132         : constant Character := Character'Val(132);
        NEL                  : constant Character := Character'Val(133);
        SSA                  : constant Character := Character'Val(134);
        ESA                  : constant Character := Character'Val(135);
        HTS                  : constant Character := Character'Val(136);
        HTJ                  : constant Character := Character'Val(137);
        VTS                  : constant Character := Character'Val(138);
        PLD                  : constant Character := Character'Val(139);
        PLU                  : constant Character := Character'Val(140);
        RI                   : constant Character := Character'Val(141);
        SS2                  : constant Character := Character'Val(142);
        SS3                  : constant Character := Character'Val(143);

18      DCS                  : constant Character := Character'Val(144);
        PU1                  : constant Character := Character'Val(145);
        PU2                  : constant Character := Character'Val(146);
        STS                  : constant Character := Character'Val(147);
        CCH                  : constant Character := Character'Val(148);
        MW                   : constant Character := Character'Val(149);
        SPA                  : constant Character := Character'Val(150);
        EPA                  : constant Character := Character'Val(151);

19      SOS                  : constant Character := Character'Val(152);
        Reserved_153         : constant Character := Character'Val(153);
        SCI                  : constant Character := Character'Val(154);
        CSI                  : constant Character := Character'Val(155);
        ST                   : constant Character := Character'Val(156);
        OSC                  : constant Character := Character'Val(157);
        PM                   : constant Character := Character'Val(158);
        APC                  : constant Character := Character'Val(159);

20  -- Other graphic characters:

21  -- Character positions 160 (16#A0#) .. 175 (16#AF#):
        No_Break_Space              : constant Character := ' ';  --Character'V\
al(160)
        NBSP                        : Character renames No_Break_Space;
        Inverted_Exclamation        : constant Character := Character'Val(161);
        Cent_Sign                   : constant Character := Character'Val(162);
        Pound_Sign                  : constant Character := Character'Val(163);
        Currency_Sign               : constant Character := Character'Val(164);
        Yen_Sign                    : constant Character := Character'Val(165);
        Broken_Bar                  : constant Character := Character'Val(166);
        Section_Sign                : constant Character := Character'Val(167);
        Diaeresis                   : constant Character := Character'Val(168);
        Copyright_Sign              : constant Character := Character'Val(169);
        Feminine_Ordinal_Indicator  : constant Character := Character'Val(170);
        Left_Angle_Quotation        : constant Character := Character'Val(171);
        Not_Sign                    : constant Character := Character'Val(172);
        Soft_Hyphen                 : constant Character := Character'Val(173);
        Registered_Trade_Mark_Sign  : constant Character := Character'Val(174);
        Macron                      : constant Character := Character'Val(175);

22  -- Character positions 176 (16#B0#) .. 191 (16#BF#):
        Degree_Sign                 : constant Character := Character'Val(176);
        Ring_Above                  : Character renames Degree_Sign;
        Plus_Minus_Sign             : constant Character := Character'Val(177);
        Superscript_Two             : constant Character := Character'Val(178);
        Superscript_Three           : constant Character := Character'Val(179);
        Acute                       : constant Character := Character'Val(180);
        Micro_Sign                  : constant Character := Character'Val(181);
        Pilcrow_Sign                : constant Character := Character'Val(182);
        Paragraph_Sign              : Character renames Pilcrow_Sign;
        Middle_Dot                  : constant Character := Character'Val(183);
        Cedilla                     : constant Character := Character'Val(184);
        Superscript_One             : constant Character := Character'Val(185);
        Masculine_Ordinal_Indicator : constant Character := Character'Val(186);
        Right_Angle_Quotation       : constant Character := Character'Val(187);
        Fraction_One_Quarter        : constant Character := Character'Val(188);
        Fraction_One_Half           : constant Character := Character'Val(189);
        Fraction_Three_Quarters     : constant Character := Character'Val(190);
        Inverted_Question           : constant Character := Character'Val(191);

23  -- Character positions 192 (16#C0#) .. 207 (16#CF#):
        UC_A_Grave                  : constant Character := Character'Val(192);
        UC_A_Acute                  : constant Character := Character'Val(193);
        UC_A_Circumflex             : constant Character := Character'Val(194);
        UC_A_Tilde                  : constant Character := Character'Val(195);
        UC_A_Diaeresis              : constant Character := Character'Val(196);
        UC_A_Ring                   : constant Character := Character'Val(197);
        UC_AE_Diphthong             : constant Character := Character'Val(198);
        UC_C_Cedilla                : constant Character := Character'Val(199);
        UC_E_Grave                  : constant Character := Character'Val(200);
        UC_E_Acute                  : constant Character := Character'Val(201);
        UC_E_Circumflex             : constant Character := Character'Val(202);
        UC_E_Diaeresis              : constant Character := Character'Val(203);
        UC_I_Grave                  : constant Character := Character'Val(204);
        UC_I_Acute                  : constant Character := Character'Val(205);
        UC_I_Circumflex             : constant Character := Character'Val(206);
        UC_I_Diaeresis              : constant Character := Character'Val(207);

24  -- Character positions 208 (16#D0#) .. 223 (16#DF#):
        UC_Icelandic_Eth            : constant Character := Character'Val(208);
        UC_N_Tilde                  : constant Character := Character'Val(209);
        UC_O_Grave                  : constant Character := Character'Val(210);
        UC_O_Acute                  : constant Character := Character'Val(211);
        UC_O_Circumflex             : constant Character := Character'Val(212);
        UC_O_Tilde                  : constant Character := Character'Val(213);
        UC_O_Diaeresis              : constant Character := Character'Val(214);
        Multiplication_Sign         : constant Character := Character'Val(215);
        UC_O_Oblique_Stroke         : constant Character := Character'Val(216);
        UC_U_Grave                  : constant Character := Character'Val(217);
        UC_U_Acute                  : constant Character := Character'Val(218);
        UC_U_Circumflex             : constant Character := Character'Val(219);
        UC_U_Diaeresis              : constant Character := Character'Val(220);
        UC_Y_Acute                  : constant Character := Character'Val(221);
        UC_Icelandic_Thorn          : constant Character := Character'Val(222);
        LC_German_Sharp_S           : constant Character := Character'Val(223);

25  -- Character positions 224 (16#E0#) .. 239 (16#EF#):
        LC_A_Grave                  : constant Character := Character'Val(224);
        LC_A_Acute                  : constant Character := Character'Val(225);
        LC_A_Circumflex             : constant Character := Character'Val(226);
        LC_A_Tilde                  : constant Character := Character'Val(227);
        LC_A_Diaeresis              : constant Character := Character'Val(228);
        LC_A_Ring                   : constant Character := Character'Val(229);
        LC_AE_Diphthong             : constant Character := Character'Val(230);
        LC_C_Cedilla                : constant Character := Character'Val(231);
        LC_E_Grave                  : constant Character := Character'Val(232);
        LC_E_Acute                  : constant Character := Character'Val(233);
        LC_E_Circumflex             : constant Character := Character'Val(234);
        LC_E_Diaeresis              : constant Character := Character'Val(235);
        LC_I_Grave                  : constant Character := Character'Val(236);
        LC_I_Acute                  : constant Character := Character'Val(237);
        LC_I_Circumflex             : constant Character := Character'Val(238);
        LC_I_Diaeresis              : constant Character := Character'Val(239);

26  -- Character positions 240 (16#F0#) .. 255 (16#FF#):
        LC_Icelandic_Eth            : constant Character := Character'Val(240);
        LC_N_Tilde                  : constant Character := Character'Val(241);
        LC_O_Grave                  : constant Character := Character'Val(242);
        LC_O_Acute                  : constant Character := Character'Val(243);
        LC_O_Circumflex             : constant Character := Character'Val(244);
        LC_O_Tilde                  : constant Character := Character'Val(245);
        LC_O_Diaeresis              : constant Character := Character'Val(246);
        Division_Sign               : constant Character := Character'Val(247);
        LC_O_Oblique_Stroke         : constant Character := Character'Val(248);
        LC_U_Grave                  : constant Character := Character'Val(249);
        LC_U_Acute                  : constant Character := Character'Val(250);
        LC_U_Circumflex             : constant Character := Character'Val(251);
        LC_U_Diaeresis              : constant Character := Character'Val(252);
        LC_Y_Acute                  : constant Character := Character'Val(253);
        LC_Icelandic_Thorn          : constant Character := Character'Val(254);
        LC_Y_Diaeresis              : constant Character := Character'Val(255);
    end Ada.Characters.Latin_1;

{94-4488.a} {94-4709.a} {94-4726.a} {94-4982.a}


                         Implementation Permissions

27   An implementation may provide additional packages as children of
Ada.Characters, to declare names for the symbols of the local character set
or other character sets.



A.4 String Handling

1   This clause presents the specifications of the package Strings and
several child packages, which provide facilities for dealing with string
data.  Fixed-length, bounded-length, and unbounded-length strings are
supported, for both String and Wide_String.  The string-handling subprograms
include searches for pattern strings and for characters in program-specified
sets, translation (via a character-to-character mapping), and transformation
(replacing, inserting, overwriting, and deleting of substrings).


                            Extensions to Ada 83

        1.a   {extensions to Ada 83} This clause is new to Ada 9X.



A.4.1 The Package Strings

1   The package Strings provides declarations common to the string handling
packages.


                              Static Semantics

2   The library package Strings has the following declaration:

3   package Ada.Strings is
       pragma Pure(Strings);

4      Space      : constant Character      := ' ';
       Wide_Space : constant Wide_Character := ' ';

5      Length_Error, Pattern_Error, Index_Error, Translation_Error : exception;

6      type Alignment  is (Left, Right, Center);
       type Truncation is (Left, Right, Error);
       type Membership is (Inside, Outside);
       type Direction  is (Forward, Backward);
       type Trim_End   is (Left, Right, Both);
    end Ada.Strings;



A.4.2 The Package Strings.Maps

1   The package Strings.Maps defines the types, operations, and other
entities needed for character sets and character-to-character mappings.


                              Static Semantics

2   The library package Strings.Maps has the following declaration:

3   package Ada.Strings.Maps is
       pragma Preelaborate(Maps);

4      -- Representation for a set of character values:
       type Character_Set is private;

5      Null_Set : constant Character_Set;

6      type Character_Range is
         record
            Low  : Character;
            High : Character;
         end record;
       -- Represents Character range Low..High

7      type Character_Ranges is array (Positive range <>) of Character_Range;

8      function To_Set    (Ranges : in Character_Ranges) return Character_Set;

9      function To_Set    (Span   : in Character_Range)  return Character_Set;

10     function To_Ranges (Set    : in Character_Set)    return Character_Range\
s;

11     function "="   (Left, Right : in Character_Set) return Boolean;

12     function "not" (Right : in Character_Set)       return Character_Set;
       function "and" (Left, Right : in Character_Set) return Character_Set;
       function "or"  (Left, Right : in Character_Set) return Character_Set;
       function "xor" (Left, Right : in Character_Set) return Character_Set;
       function "-"   (Left, Right : in Character_Set) return Character_Set;

13     function Is_In (Element : in Character;
                       Set     : in Character_Set)
          return Boolean;

14     function Is_Subset (Elements : in Character_Set;
                           Set      : in Character_Set)
          return Boolean;

15     function "<=" (Left  : in Character_Set;
                      Right : in Character_Set)
          return Boolean renames Is_Subset;

16     -- Alternative representation for a set of character values:
       subtype Character_Sequence is String;

17     function To_Set (Sequence  : in Character_Sequence) return Character_Set;

18     function To_Set (Singleton : in Character)          return Character_Set;

19     function To_Sequence (Set  : in Character_Set)      return Character_Seq\
uence;

20     -- Representation for a character to character mapping:
       type Character_Mapping is private;

21     function Value (Map     : in Character_Mapping;
                       Element : in Character)
          return Character;

22     Identity : constant Character_Mapping;

23     function To_Mapping (From, To : in Character_Sequence) return Character_\
Mapping;

24     function To_Domain (Map : in Character_Mapping) return Character_Sequenc\
e;
       function To_Range  (Map : in Character_Mapping) return Character_Sequenc\
e;

25     type Character_Mapping_Function is
          access function (From : in Character) return Character;

26  private
       ... -- not specified by the language
    end Ada.Strings.Maps;

{94-4606.a}

27   An object of type Character_Set represents a set of characters.

28   Null_Set represents the set containing no characters.

29   An object Obj of type Character_Range represents the set of characters
in the range Obj.Low .. Obj.High.

30   An object Obj of type Character_Ranges represents the union of the sets
corresponding to Obj(I) for I in Obj'Range.
31  function To_Set (Ranges : in Character_Ranges) return Character_Set;

        32   If Ranges'Length=0 then Null_Set is returned; otherwise the
        returned value represents the set corresponding to Ranges.


33  function To_Set (Span : in Character_Range) return Character_Set;

        34   The returned value represents the set containing each character
        in Span.


35  function To_Ranges (Set : in Character_Set) return Character_Ranges;

        36   If Set = Null_Set then an empty Character_Ranges array is
        returned; otherwise the shortest array of contiguous ranges of
        Character values in Set, in increasing order of Low, is returned.


37  function "=" (Left, Right : in Character_Set) return Boolean;

        {94-4606.a}
        38   The function "=" returns True if Left and Right represent
        identical sets, and False otherwise.

39   Each of the logical operators "not", "and", "or", and "xor" returns a
Character_Set value that represents the set obtained by applying the
corresponding operation to the set(s) represented by the parameter(s) of the
operator.  "-"(Left, Right) is equivalent to "and"(Left, "not"(Right)).

        39.a   Reason:  The set minus operator is provided for efficiency.


40  function Is_In (Element : in Character;
                    Set     : in Character_Set);
       return Boolean;

        41   Is_In returns True if Element is in Set, and False otherwise.


42  function Is_Subset (Elements : in Character_Set;
                        Set      : in Character_Set)
       return Boolean;

        43   Is_Subset returns True if Elements is a subset of Set, and False
        otherwise.


44  subtype Character_Sequence is String;

        45   The Character_Sequence subtype is used to portray a set of
        character values and also to identify the domain and range of a
        character mapping.

        45.a   Reason:  Although a named subtype is redundant -- the
        predefined type String could have been used for the parameter to To_
        Set and To_Mapping below -- the use of a differently named subtype
        identifies the intended purpose of the parameter.


46  function To_Set (Sequence  : in Character_Sequence) return Character_Set;

    function To_Set (Singleton : in Character)          return Character_Set;

        47   Sequence portrays the set of character values that it explicitly
        contains (ignoring duplicates).  Singleton portrays the set
        comprising a single Character.  Each of the To_Set functions returns
        a Character_Set value that represents the set portrayed by Sequence
        or Singleton.


48  function To_Sequence (Set : in Character_Set) return Character_Sequence;

        49   The function To_Sequence returns a Character_Sequence value
        containing each of the characters in the set represented by Set, in
        ascending order with no duplicates.


50  type Character_Mapping is private;

        51   An object of type Character_Mapping represents a Character-to-
        Character mapping.


52  function Value (Map     : in Character_Mapping;
                    Element : in Character)
       return Character;

        53   The function Value returns the Character value to which Element
        maps with respect to the mapping represented by Map.

54   {match (a character to a pattern character)} A character C matches a
pattern character P with respect to a given Character_Mapping value Map if
Value(Map, C) = P. {match (a string to a pattern string)} A string S matches
a pattern string P with respect to a given Character_Mapping if their lengths
are the same and if each character in S matches its corresponding character
in the pattern string P.

        54.a   Discussion:  In an earlier version of the string handling
        packages, the definition of matching was symmetrical, namely C
        matches P if Value(Map,C) = Value(Map,P).  However, applying the
        mapping to the pattern was confusing according to some reviewers.
        Furthermore, if the symmetrical version is needed, it can be achieved
        by applying the mapping to the pattern (via translation) prior to
        passing it as a parameter.

55   String handling subprograms that deal with character mappings have
parameters whose type is Character_Mapping.


56  Identity : constant Character_Mapping;

        57   Identity maps each Character to itself.


58  function To_Mapping (From, To : in Character_Sequence) return Character_Map\
ping;

        {94-4606.a}
        59   To_Mapping produces a Character_Mapping such that each element
        of From maps to the corresponding element of To, and each other
        character maps to itself.  If From'Length /= To'Length, or if some
        character is repeated in From, then Translation_Error is propagated.


60  function To_Domain (Map : in Character_Mapping) return Character_Sequence;

        61   To_Domain returns the shortest Character_Sequence value D such
        that each character not in D maps to itself, and such that the
        characters in D are in ascending order.  The lower bound of D is 1.


62  function To_Range  (Map : in Character_Mapping) return Character_Sequence;

        63   To_Range returns the Character_Sequence value R, with lower
        bound 1 and upper bound Map'Length, {94-4497.a} such that if D = To_
        Domain(Map) then D(I) maps to R(I) for each I in D'Range.

64   An object F of type Character_Mapping_Function maps a Character value C
to the Character value F.all(C), which is said to match C with respect to
mapping function F. {match (a character to a pattern character, with respect
to a character mapping function)}


     NOTES
65   (7) Character_Mapping and Character_Mapping_Function are used both for
     character equivalence mappings in the search subprograms (such as for
     case insensitivity) and as transformational mappings in the Translate
     subprograms.

66   (8) To_Domain(Identity) and To_Range(Identity) each returns the null
     string.

   66.a   Reason:  Package Strings.Maps is not pure, since it declares an
        access-to-subprogram type.

     {94-4970.a}


                                  Examples

67   To_Mapping("ABCD", "ZZAB") returns a Character_Mapping that maps 'A' and
'B' to 'Z', 'C' to 'A', 'D' to 'B', and each other Character to itself.



A.4.3 Fixed-Length String Handling

1   The language-defined package Strings.Fixed provides string-handling
subprograms for fixed-length strings; that is, for values of type
Standard.String.  Several of these subprograms are procedures that modify the
contents of a String that is passed as an out or an in out parameter; each
has additional parameters to control the effect when the logical length of
the result differs from the parameter's length.

2   For each function that returns a String, the lower bound of the returned
value is 1.

        2.a   Discussion:  Most operations that yields a String are provided
        both as a function and as a procedure.  The functional form is
        possibly a more aesthetic style but may introduce overhead due to
        extra copying or dynamic memory usage in some implementations.  Thus
        a procedural form, with an in out parameter so that all copying is
        done `in place', is also supplied.

3   The basic model embodied in the package is that a fixed-length string
comprises significant characters and possibly padding (with space characters)
on either or both ends.  When a shorter string is copied to a longer string,
padding is inserted, and when a longer string is copied to a shorter one,
padding is stripped.  The Move procedure in Strings.Fixed, which takes a
String as an out parameter, allows the programmer to control these effects.
Similar control is provided by the string transformation procedures.


                              Static Semantics

4   The library package Strings.Fixed has the following declaration:

5   with Ada.Strings.Maps;
    package Ada.Strings.Fixed is
       pragma Preelaborate(Fixed);
6   -- "Copy" procedure for strings of possibly different lengths

7      procedure Move (Source  : in  String;
                       Target  : out String;
                       Drop    : in  Truncation := Error;
                       Justify : in  Alignment  := Left;
                       Pad     : in  Character  := Space);

8   -- Search subprograms

9      function Index (Source   : in String;
                       Pattern  : in String;
                       Going    : in Direction := Forward;
                       Mapping  : in Maps.Character_Mapping
                                    := Maps.Identity)
          return Natural;

10     function Index (Source   : in String;
                       Pattern  : in String;
                       Going    : in Direction := Forward;
                       Mapping  : in Maps.Character_Mapping_Function)
          return Natural;

11     function Index (Source : in String;
                       Set    : in Maps.Character_Set;
                       Test   : in Membership := Inside;
                       Going  : in Direction  := Forward)
          return Natural;

12     function Index_Non_Blank (Source : in String;
                                 Going  : in Direction := Forward)
          return Natural;

13     function Count (Source   : in String;
                       Pattern  : in String;
                       Mapping  : in Maps.Character_Mapping
                                     := Maps.Identity)
          return Natural;

14     function Count (Source   : in String;
                       Pattern  : in String;
                       Mapping  : in Maps.Character_Mapping_Function)
          return Natural;

15     function Count (Source   : in String;
                       Set      : in Maps.Character_Set)
          return Natural;

16     procedure Find_Token (Source : in String;
                             Set    : in Maps.Character_Set;
                             Test   : in Membership;
                             First  : out Positive;
                             Last   : out Natural);

17  -- String translation subprograms

18     function Translate (Source  : in String;
                           Mapping : in Maps.Character_Mapping)
          return String;

19     procedure Translate (Source  : in out String;
                            Mapping : in Maps.Character_Mapping);

20     function Translate (Source  : in String;
                           Mapping : in Maps.Character_Mapping_Function)
          return String;

21     procedure Translate (Source  : in out String;
                            Mapping : in Maps.Character_Mapping_Function);

22  -- String transformation subprograms

23     function Replace_Slice (Source   : in String;
                               Low      : in Positive;
                               High     : in Natural;
                               By       : in String)
          return String;

24     procedure Replace_Slice (Source   : in out String;
                                Low      : in Positive;
                                High     : in Natural;
                                By       : in String;
                                Drop     : in Truncation := Error;
                                Justify  : in Alignment  := Left;
                                Pad      : in Character  := Space);

25     function Insert (Source   : in String;
                        Before   : in Positive;
                        New_Item : in String)
          return String;

26     procedure Insert (Source   : in out String;
                         Before   : in Positive;
                         New_Item : in String;
                         Drop     : in Truncation := Error);

27     function Overwrite (Source   : in String;
                           Position : in Positive;
                           New_Item : in String)
          return String;

28     procedure Overwrite (Source   : in out String;
                            Position : in Positive;
                            New_Item : in String;
                            Drop     : in Truncation := Right);

29     function Delete (Source  : in String;
                        From    : in Positive;
                        Through : in Natural)
          return String;

30     procedure Delete (Source  : in out String;
                         From    : in Positive;
                         Through : in Natural;
                         Justify : in Alignment := Left;
                         Pad     : in Character := Space);

31   --String selector subprograms
       function Trim (Source : in String;
                      Side   : in Trim_End)
          return String;

32     procedure Trim (Source  : in out String;
                       Side    : in Trim_End;
                       Justify : in Alignment := Left;
                       Pad     : in Character := Space);

33     function Trim (Source : in String;
                      Left   : in Maps.Character_Set;
                      Right  : in Maps.Character_Set)
          return String;

34     procedure Trim (Source  : in out String;
                       Left    : in Maps.Character_Set;
                       Right   : in Maps.Character_Set;
                       Justify : in Alignment := Strings.Left;
                       Pad     : in Character := Space);

35     function Head (Source : in String;
                      Count  : in Natural;
                      Pad    : in Character := Space)
          return String;

36     procedure Head (Source  : in out String;
                       Count   : in Natural;
                       Justify : in Alignment := Left;
                       Pad     : in Character := Space);

37     function Tail (Source : in String;
                      Count  : in Natural;
                      Pad    : in Character := Space)
          return String;

38     procedure Tail (Source  : in out String;
                       Count   : in Natural;
                       Justify : in Alignment := Left;
                       Pad     : in Character := Space);

39  --String constructor functions

40     function "*" (Left  : in Natural;
                     Right : in Character) return String;

41     function "*" (Left  : in Natural;
                     Right : in String) return String;

42  end Ada.Strings.Fixed;

{94-4471.a}

43   The effects of the above subprograms are as follows.


44  procedure Move (Source  : in  String;
                    Target  : out String;
                    Drop    : in  Truncation := Error;
                    Justify : in  Alignment  := Left;
                    Pad     : in  Character  := Space);

        45   The Move procedure copies characters from Source to Target.  If
        Source has the same length as Target, then the effect is to assign
        Source to Target.  If Source is shorter than Target then:

           46  If Justify=Left, then Source is copied into the first
               Source'Length characters of Target.

           47  If Justify=Right, then Source is copied into the last
               Source'Length characters of Target.

           48  If Justify=Center, then Source is copied into the middle
               Source'Length characters of Target.  In this case, if the
               difference in length between Target and Source is odd,
               then the extra Pad character is on the right.

           49  Pad is copied to each Target character not otherwise
               assigned.

        50   If Source is longer than Target, then the effect is based on
        Drop.
           51  If Drop=Left, then the rightmost Target'Length characters
               of Source are copied into Target.

           52  If Drop=Right, then the leftmost Target'Length characters
               of Source are copied into Target.

           53  If Drop=Error, then the effect depends on the value of
               the Justify parameter and also on whether any characters
               in Source other than Pad would fail to be copied:

                  54  If Justify=Left, and if each of the rightmost
                      Source'Length-Target'Length characters in Source
                      is Pad, then the leftmost Target'Length characters
                      of Source are copied to Target.

                  55  If Justify=Right, and if each of the leftmost
                      Source'Length-Target'Length characters in Source
                      is Pad, then the rightmost Target'Length
                      characters of Source are copied to Target.

                  56  Otherwise, Length_Error is propagated.

        56.a   Ramification:  The Move procedure will work even if Source and
        Target overlap.

        56.b   Reason:  The order of parameters (Source before Target)
        corresponds to the order in COBOL's MOVE verb.


57  function Index (Source   : in String;
                    Pattern  : in String;
                    Going    : in Direction := Forward;
                    Mapping  : in Maps.Character_Mapping
                                  := Maps.Identity)
       return Natural;

    function Index (Source   : in String;
                    Pattern  : in String;
                    Going    : in Direction := Forward;
                    Mapping  : in Maps.Character_Mapping_Function)
       return Natural;

        58   Each Index function searches for a slice of Source, with length
        Pattern'Length, that matches Pattern with respect to Mapping; the
        parameter Going indicates the direction of the lookup.  If Going =
        Forward, then Index returns the smallest index I such that the slice
        of Source starting at I matches Pattern.  If Going = Backward, then
        Index returns the largest index I such that the slice of Source
        starting at I matches Pattern.  If there is no such slice, then 0 is
        returned.  If Pattern is the null string then Pattern_Error is
        propagated.

        58.a   Discussion:  There is no default value for the Mapping
        parameter that is a Character_Mapping_Function; if there were, a call
        would be ambiguous since there is also a default for the Mapping
        parameter that is a Character_Mapping.


59  function Index (Source : in String;
                    Set    : in Maps.Character_Set;
                    Test   : in Membership := Inside;
                    Going  : in Direction  := Forward)
       return Natural;

        60   Index searches for the first or last occurrence of any of a set
        of characters (when Test=Inside), or any of the complement of a set
        of characters (when Test=Outside).  It returns the smallest index I
        (if Going=Forward) or the largest index I (if Going=Backward) such
        that Source(I) satisfies the Test condition with respect to Set; it
        returns 0 if there is no such Character in Source.


61  function Index_Non_Blank (Source : in String;
                              Going  : in Direction := Forward)
       return Natural;

        62   Returns Index(Source, Maps.To_Set(Space), Outside, Going)


63  function Count (Source   : in String;
                    Pattern  : in String;
                    Mapping  : in Maps.Character_Mapping
                                 := Maps.Identity)
       return Natural;

    function Count (Source   : in String;
                    Pattern  : in String;
                    Mapping  : in Maps.Character_Mapping_Function)
       return Natural;

        64   Returns the maximum number of nonoverlapping slices of Source
        that match Pattern with respect to Mapping.  If Pattern is the null
        string then Pattern_Error is propagated.

        64.a   Reason:  We say `maximum number' because it is possible to
        slice a source string in different ways yielding different numbers of
        matches.  For example if Source is "ABABABA" and Pattern is "ABA",
        then Count yields 2, although there is a partitioning of Source that
        yields just 1 match, for the middle slice.  Saying `maximum number'
        is equivalent to saying that the pattern match starts either at the
        low index or the high index position.


65  function Count (Source   : in String;
                    Set      : in Maps.Character_Set)
       return Natural;

        66   Returns the number of occurrences in Source of characters that
        are in Set.


67  procedure Find_Token (Source : in String;
                          Set    : in Maps.Character_Set;
                          Test   : in Membership;
                          First  : out Positive;
                          Last   : out Natural);

        68   Find_Token returns in First and Last the indices of the
        beginning and end of the first slice of Source all of whose elements
        satisfy the Test condition, and such that the elements (if any)
        immediately before and after the slice do not satisfy the Test
        condition.  If no such slice exists, then the value returned for Last
        is zero, and the value returned for First is Source'First.


69  function Translate (Source  : in String;
                        Mapping : in Maps.Character_Mapping)
       return String;

    function Translate (Source  : in String;
                        Mapping : in Maps.Character_Mapping_Function)
       return String;

        70   Returns the string S whose length is Source'Length and such that
        S(I) is the character to which Mapping maps the corresponding element
        of Source, for I in 1..Source'Length.


71  procedure Translate (Source  : in out String;
                         Mapping : in Maps.Character_Mapping);

    procedure Translate (Source  : in out String;
                         Mapping : in Maps.Character_Mapping_Function);

        72   Equivalent to Source := Translate(Source, Mapping).


73  function Replace_Slice (Source   : in String;
                            Low      : in Positive;
                            High     : in Natural;
                            By       : in String)
       return String;

        74   If Low > Source'Last+1, or High < Source'First-1, then Index_
        Error is propagated.  Otherwise, if High >= Low then the returned
        string comprises Source(Source'First..Low-1) & By &
        Source(High+1..Source'Last), and if High < Low then the returned
        string is Insert(Source, Before=>Low, New_Item=>By).


75  procedure Replace_Slice (Source   : in out String;
                             Low      : in Positive;
                             High     : in Natural;
                             By       : in String;
                             Drop     : in Truncation := Error;
                             Justify  : in Alignment  := Left;
                             Pad      : in Character  := Space);

        76   Equivalent to Move(Replace_Slice(Source, Low, High, By), Source,
        Drop, Justify, Pad).


77  function Insert (Source   : in String;
                     Before   : in Positive;
                     New_Item : in String)
       return String;

        78   Propagates Index_Error if Before is not in Source'First ..
        Source'Last+1; otherwise returns Source(Source'First..Before-1) &
        New_Item & Source(Before..Source'Last), but with lower bound 1.


79  procedure Insert (Source   : in out String;
                      Before   : in Positive;
                      New_Item : in String;
                      Drop     : in Truncation := Error);

        80   Equivalent to Move(Insert(Source, Before, New_Item), Source,
        Drop).


81  function Overwrite (Source   : in String;
                        Position : in Positive;
                        New_Item : in String)
       return String;

        82   Propagates Index_Error if Position is not in Source'First ..
        Source'Last+1; otherwise returns the string obtained from Source by
        consecutively replacing characters starting at Position with
        corresponding characters from New_Item.  If the end of Source is
        reached before the characters in New_Item are exhausted, the
        remaining characters from New_Item are appended to the string.


83  procedure Overwrite (Source   : in out String;
                         Position : in Positive;
                         New_Item : in String;
                         Drop     : in Truncation := Right);

        84   Equivalent to Move(Overwrite(Source, Position, New_Item),
        Source, Drop).


85  function Delete (Source  : in String;
                     From    : in Positive;
                     Through : in Natural)
       return String;

        86   If From <= Through, the returned string is Replace_Slice(Source,
        From, Through, ""), otherwise it is Source.


87  procedure Delete (Source  : in out String;
                      From    : in Positive;
                      Through : in Natural;
                      Justify : in Alignment := Left;
                      Pad     : in Character := Space);

        88   Equivalent to Move(Delete(Source, From, Through), Source,
        Justify => Justify, Pad => Pad).


89  function Trim (Source : in String;
                   Side   : in Trim_End)
      return String;

        90   Returns the string obtained by removing from Source all leading
        Space characters (if Side = Left), all trailing Space characters (if
        Side = Right), or all leading and trailing Space characters (if Side
        = Both).


91  procedure Trim (Source  : in out String;
                    Side    : in Trim_End;
                    Justify : in Alignment := Left;
                    Pad     : in Character := Space);

        {94-4498.b} {94-4768.q} {94-4852.a} {94-4876.a} {94-4883.a}
        92   Equivalent to Move(Trim(Source, Side), Source, Justify=>Justify,
        Pad=>Pad).


93  function Trim (Source : in String;
                   Left   : in Maps.Character_Set;
                   Right  : in Maps.Character_Set)
       return String;

        94   Returns the string obtained by removing from Source all leading
        characters in Left and all trailing characters in Right.


95  procedure Trim (Source  : in out String;
                    Left    : in Maps.Character_Set;
                    Right   : in Maps.Character_Set;
                    Justify : in Alignment := Strings.Left;
                    Pad     : in Character := Space);

        96   Equivalent to Move(Trim(Source, Left, Right), Source, Justify =>
        Justify, Pad=>Pad).


97  function Head (Source : in String;
                   Count  : in Natural;
                   Pad    : in Character := Space)
       return String;

        98   Returns a string of length Count.  If Count <= Source'Length,
        the string comprises the first Count characters of Source.  Otherwise
        its contents are Source concatenated with Count-Source'Length Pad
        characters.


99  procedure Head (Source  : in out String;
                    Count   : in Natural;
                    Justify : in Alignment := Left;
                    Pad     : in Character := Space);

        100   Equivalent to Move(Head(Source, Count, Pad), Source,
        Drop=>Error, Justify=>Justify, Pad=>Pad).


101 function Tail (Source : in String;
                   Count  : in Natural;
                   Pad    : in Character := Space)
       return String;

        102   Returns a string of length Count.  If Count <= Source'Length,
        the string comprises the last Count characters of Source.  Otherwise
        its contents are Count-Source'Length Pad characters concatenated with
        Source.


103 procedure Tail (Source  : in out String;
                    Count   : in Natural;
                    Justify : in Alignment := Left;
                    Pad     : in Character := Space);

        104   Equivalent to Move(Tail(Source, Count, Pad), Source,
        Drop=>Error, Justify=>Justify, Pad=>Pad).


105 function "*" (Left  : in Natural;
                  Right : in Character) return String;

    function "*" (Left  : in Natural;
                  Right : in String) return String;

        106   These functions replicate a character or string a specified
        number of times.  The first function returns a string whose length is
        Left and each of whose elements is Right.  The second function
        returns a string whose length is Left*Right'Length and whose value is
        the null string if Left = 0 and is (Left-1)*Right & Right otherwise.


     NOTES
107  (9) In the Index and Count functions taking Pattern and Mapping
     parameters, the actual String parameter passed to Pattern should
     comprise characters occurring as target characters of the mapping.
     Otherwise the pattern will not match.

108  (10) In the Insert subprograms, inserting at the end of a string is
     obtained by passing Source'Last+1 as the Before parameter.

109  (11) {Constraint_Error (raised by failure of run-time check)} If a null
     Character_Mapping_Function is passed to any of the string handling
     subprograms, Constraint_Error is propagated.



A.4.4 Bounded-Length String Handling

1   The language-defined package Strings.Bounded provides a generic package
each of whose instances yields a private type Bounded_String and a set of
operations.  An object of a particular Bounded_String type represents a
String whose low bound is 1 and whose length can vary conceptually between 0
and a maximum size established at the generic instantiation.  {94-4971.a} The
subprograms for fixed-length string handling are either overloaded directly
for Bounded_String, or are modified as needed to reflect the variability in
length.  Additionally, since the Bounded_String type is private, appropriate
constructor and selector operations are provided.

        1.a   Reason:  Strings.Bounded declares an inner generic package,
        versus itself being directly a generic child of Strings, in order to
        retain compatibility with a version of the string-handling packages
        that is generic with respect to the character and string types.

        1.b   Reason:  The bound of a bounded-length string is specified as a
        parameter to a generic, versus as the value for a discriminant,
        because of the inappropriateness of assignment and equality of
        discriminated types for the copying and comparison of bounded
        strings.


                              Static Semantics

2   The library package Strings.Bounded has the following declaration:

3   with Ada.Strings.Maps;
    package Ada.Strings.Bounded is
       pragma Preelaborate(Bounded);

4      generic
          Max   : Positive;    -- Maximum length of a Bounded_String
       package Generic_Bounded_Length is

5         Max_Length : constant Positive := Max;

6         type Bounded_String is private;

7         Null_Bounded_String : constant Bounded_String;

8         subtype Length_Range is Natural range 0 .. Max_Length;

9         function Length (Source : in Bounded_String) return Length_Range;

10     -- Conversion, Concatenation, and Selection functions

11        function To_Bounded_String (Source : in String;
                                      Drop   : in Truncation := Error)
             return Bounded_String;

12        function To_String (Source : in Bounded_String) return String;

13        function Append (Left, Right : in Bounded_String;
                           Drop        : in Truncation  := Error)
             return Bounded_String;

14        function Append (Left  : in Bounded_String;
                           Right : in String;
                           Drop  : in Truncation := Error)
             return Bounded_String;

15        function Append (Left  : in String;
                           Right : in Bounded_String;
                           Drop  : in Truncation := Error)
             return Bounded_String;

16        function Append (Left  : in Bounded_String;
                           Right : in Character;
                           Drop  : in Truncation := Error)
             return Bounded_String;

17        function Append (Left  : in Character;
                           Right : in Bounded_String;
                           Drop  : in Truncation := Error)
             return Bounded_String;

18        procedure Append (Source   : in out Bounded_String;
                            New_Item : in Bounded_String;
                            Drop     : in Truncation  := Error);

19        procedure Append (Source   : in out Bounded_String;
                            New_Item : in String;
                            Drop     : in Truncation  := Error);

20        procedure Append (Source   : in out Bounded_String;
                            New_Item : in Character;
                            Drop     : in Truncation  := Error);

21        function "&" (Left, Right : in Bounded_String)
             return Bounded_String;

22        function "&" (Left : in Bounded_String; Right : in String)
             return Bounded_String;

23        function "&" (Left : in String; Right : in Bounded_String)
             return Bounded_String;

24        function "&" (Left : in Bounded_String; Right : in Character)
             return Bounded_String;

25        function "&" (Left : in Character; Right : in Bounded_String)
             return Bounded_String;

26        function Element (Source : in Bounded_String;
                            Index  : in Positive)
             return Character;

27        procedure Replace_Element (Source : in out Bounded_String;
                                     Index  : in Positive;
                                     By     : in Character);

28        function Slice (Source : in Bounded_String;
                          Low    : in Positive;
                          High   : in Natural)
             return String;

29        function "="  (Left, Right : in Bounded_String) return Boolean;
          function "="  (Left : in Bounded_String; Right : in String)
            return Boolean;

30        function "="  (Left : in String; Right : in Bounded_String)
            return Boolean;

31        function "<"  (Left, Right : in Bounded_String) return Boolean;

32        function "<"  (Left : in Bounded_String; Right : in String)
            return Boolean;

33        function "<"  (Left : in String; Right : in Bounded_String)
            return Boolean;

34        function "<=" (Left, Right : in Bounded_String) return Boolean;

35        function "<="  (Left : in Bounded_String; Right : in String)
            return Boolean;

36        function "<="  (Left : in String; Right : in Bounded_String)
            return Boolean;

37        function ">"  (Left, Right : in Bounded_String) return Boolean;

38        function ">"  (Left : in Bounded_String; Right : in String)
            return Boolean;

39        function ">"  (Left : in String; Right : in Bounded_String)
            return Boolean;

40        function ">=" (Left, Right : in Bounded_String) return Boolean;

41        function ">="  (Left : in Bounded_String; Right : in String)
            return Boolean;

42        function ">="  (Left : in String; Right : in Bounded_String)
            return Boolean;

43     -- Search functions

44        function Index (Source   : in Bounded_String;
                          Pattern  : in String;
                          Going    : in Direction := Forward;
                          Mapping  : in Maps.Character_Mapping
                                     := Maps.Identity)
             return Natural;

45        function Index (Source   : in Bounded_String;
                          Pattern  : in String;
                          Going    : in Direction := Forward;
                          Mapping  : in Maps.Character_Mapping_Function)
             return Natural;

46        function Index (Source : in Bounded_String;
                          Set    : in Maps.Character_Set;
                          Test   : in Membership := Inside;
                          Going  : in Direction  := Forward)
             return Natural;

47        function Index_Non_Blank (Source : in Bounded_String;
                                    Going  : in Direction := Forward)
             return Natural;

48        function Count (Source   : in Bounded_String;
                          Pattern  : in String;
                          Mapping  : in Maps.Character_Mapping
                                       := Maps.Identity)
             return Natural;

49        function Count (Source   : in Bounded_String;
                          Pattern  : in String;
                          Mapping  : in Maps.Character_Mapping_Function)
             return Natural;

50        function Count (Source   : in Bounded_String;
                          Set      : in Maps.Character_Set)
             return Natural;

51        procedure Find_Token (Source : in Bounded_String;
                                Set    : in Maps.Character_Set;
                                Test   : in Membership;
                                First  : out Positive;
                                Last   : out Natural);

52     -- String translation subprograms

53        function Translate (Source  : in Bounded_String;
                              Mapping : in Maps.Character_Mapping)
             return Bounded_String;

54        procedure Translate (Source  : in out Bounded_String;
                               Mapping : in Maps.Character_Mapping);

55        function Translate (Source  : in Bounded_String;
                              Mapping : in Maps.Character_Mapping_Function)
             return Bounded_String;

56        procedure Translate (Source  : in out Bounded_String;
                               Mapping : in Maps.Character_Mapping_Function);

57     -- String transformation subprograms

58        function Replace_Slice (Source   : in Bounded_String;
                                  Low      : in Positive;
                                  High     : in Natural;
                                  By       : in String;
                                  Drop     : in Truncation := Error)
             return Bounded_String;

59        procedure Replace_Slice (Source   : in out Bounded_String;
                                   Low      : in Positive;
                                   High     : in Natural;
                                   By       : in String;
                                   Drop     : in Truncation := Error);

60        function Insert (Source   : in Bounded_String;
                           Before   : in Positive;
                           New_Item : in String;
                           Drop     : in Truncation := Error)
             return Bounded_String;

61        procedure Insert (Source   : in out Bounded_String;
                            Before   : in Positive;
                            New_Item : in String;
                            Drop     : in Truncation := Error);

62        function Overwrite (Source    : in Bounded_String;
                              Position  : in Positive;
                              New_Item  : in String;
                              Drop      : in Truncation := Error)
             return Bounded_String;

63        procedure Overwrite (Source    : in out Bounded_String;
                               Position  : in Positive;
                               New_Item  : in String;
                               Drop      : in Truncation := Error);

64        function Delete (Source  : in Bounded_String;
                           From    : in Positive;
                           Through : in Natural)
             return Bounded_String;
65        procedure Delete (Source  : in out Bounded_String;
                            From    : in Positive;
                            Through : in Natural);

66  --String selector subprograms

67        function Trim (Source : in Bounded_String;
                         Side   : in Trim_End)
             return Bounded_String;
          procedure Trim (Source : in out Bounded_String;
                          Side   : in Trim_End);

68        function Trim (Source : in Bounded_String;
                         Left   : in Maps.Character_Set;
                         Right  : in Maps.Character_Set)
             return Bounded_String;

69        procedure Trim (Source : in out Bounded_String;
                          Left   : in Maps.Character_Set;
                          Right  : in Maps.Character_Set);

70        function Head (Source : in Bounded_String;
                         Count  : in Natural;
                         Pad    : in Character  := Space;
                         Drop   : in Truncation := Error)
             return Bounded_String;

71        procedure Head (Source : in out Bounded_String;
                          Count  : in Natural;
                          Pad    : in Character  := Space;
                          Drop   : in Truncation := Error);

72        function Tail (Source : in Bounded_String;
                         Count  : in Natural;
                         Pad    : in Character  := Space;
                         Drop   : in Truncation := Error)
             return Bounded_String;

73        procedure Tail (Source : in out Bounded_String;
                          Count  : in Natural;
                          Pad    : in Character  := Space;
                          Drop   : in Truncation := Error);

74  --String constructor subprograms

75        function "*" (Left  : in Natural;
                        Right : in Character)
             return Bounded_String;

76        function "*" (Left  : in Natural;
                        Right : in String)
             return Bounded_String;

77        function "*" (Left  : in Natural;
                        Right : in Bounded_String)
             return Bounded_String;

78        function Replicate (Count : in Natural;
                              Item  : in Character;
                              Drop  : in Truncation := Error)
             return Bounded_String;

79        function Replicate (Count : in Natural;
                              Item  : in String;
                              Drop  : in Truncation := Error)
             return Bounded_String;

80        function Replicate (Count : in Natural;
                              Item  : in Bounded_String;
                              Drop  : in Truncation := Error)
             return Bounded_String;

81     private
           ... -- not specified by the language
       end Generic_Bounded_Length;

82  end Ada.Strings.Bounded;

83   Null_Bounded_String represents the null string.  If an object of type
Bounded_String is not otherwise initialized, it will be initialized to the
same value as Null_Bounded_String.


84  function Length (Source : in Bounded_String) return Length_Range;

        85   The Length function returns the length of the string represented
        by Source.


86  function To_Bounded_String (Source : in String;
                                Drop   : in Truncation := Error)
       return Bounded_String;

        87   If Source'Length <= Max_Length then this function returns a
        Bounded_String that represents Source.  Otherwise the effect depends
        on the value of Drop:

           88  If Drop=Left, then the result is a Bounded_String that
               represents the string comprising the rightmost Max_Length
               characters of Source.

           89  If Drop=Right, then the result is a Bounded_String that
               represents the string comprising the leftmost Max_Length
               characters of Source.

           90  If Drop=Error, then Strings.Length_Error is propagated.


91  function To_String (Source : in Bounded_String) return String;

        92   To_String returns the String value with lower bound 1
        represented by Source.  If B is a Bounded_String, then B = To_
        Bounded_String(To_String(B)).

93   Each of the Append functions returns a Bounded_String obtained by
concatenating the string or character given or represented by one of the
parameters, with the string or character given or represented by the other
parameter, and applying To_Bounded_String to the concatenation result string,
with Drop as provided to the Append function.

94   Each of the procedures Append(Source, New_Item, Drop) has the same
effect as the corresponding assignment Source := Append(Source, New_Item,
Drop).

95   Each of the "&" functions has the same effect as the corresponding
Append function, with Error as the Drop parameter.


96  function Element (Source : in Bounded_String;
                      Index  : in Positive)
       return Character;

        97   Returns the character at position Index in the string
        represented by Source; propagates Index_Error if Index >
        Length(Source).


98  procedure Replace_Element (Source : in out Bounded_String;
                               Index  : in Positive;
                               By     : in Character);

        99   Updates Source such that the character at position Index in the
        string represented by Source is By; propagates Index_Error if Index >
        Length(Source).


100 function Slice (Source : in Bounded_String;
                    Low    : in Positive;
                    High   : in Natural)
       return String;

        101   Returns the slice at positions Low through High in the string
        represented by Source; propagates Index_Error if Low >
        Length(Source)+1.

102   Each of the functions "=", "<", ">","<=", and ">=" returns the same
result as the corresponding String operation applied to the String values
given or represented by the two parameters.

103   Each of the search subprograms (Index, Index_Non_Blank, Count, Find_
Token) has the same effect as the corresponding subprogram in Strings.Fixed
applied to the string represented by the Bounded_String parameter.

104   Each of the Translate subprograms, when applied to a Bounded_String,
has an analogous effect to the corresponding subprogram in Strings.Fixed.
For the Translate function, the translation is applied to the string
represented by the Bounded_String parameter, and the result is converted (via
To_Bounded_String) to a Bounded_String.  For the Translate procedure, the
string represented by the Bounded_String parameter after the translation is
given by the Translate function for fixed-length strings applied to the
string represented by the original value of the parameter.

105   Each of the transformation subprograms (Replace_Slice, Insert,
Overwrite, Delete), selector subprograms (Trim, Head, Tail), and constructor
functions ("*") has an effect based on its corresponding subprogram in
Strings.Fixed, and Replicate is based on Fixed."*".  For each of these
subprograms, the corresponding fixed-length string subprogram is applied to
the string represented by the Bounded_String parameter.  To_Bounded_String is
applied the result string, with Drop (or Error in the case of Generic_
Bounded_Length."*") determining the effect when the string length exceeds
Max_Length.

        105.a   Ramification:  The "/=" operations between Bounded_String and
        String, and between String and Bounded_String, are automatically
        defined based on the corrsponding "=" operations.


                            Implementation Advice

106   Bounded string objects should not be implemented by implicit pointers
and dynamic allocation.

        106.a   Implementation Note:  The following is a possible
        implementation of the private part of the package:

106.b       type Bounded_String_Internals (Length : Length_Range := 0) is
               record
                  Data : String(1..Length);
               end record;
106.c       type Bounded_String is
               record
                  Data : Bounded_String_Internals;  -- Unconstrained
               end record;

106.d       Null_Bounded_String : constant Bounded_String :=
               (Data => (Length => 0,
                         Data   => (1..0 => ' ')));



A.4.5 Unbounded-Length String Handling

1   The language-defined package Strings.Unbounded provides a private type
Unbounded_String and a set of operations.  An object of type Unbounded_String
represents a String whose low bound is 1 and whose length can vary
conceptually between 0 and Natural'Last.  {94-4971.a} The subprograms for
fixed-length string handling are either overloaded directly for Unbounded_
String, or are modified as needed to reflect the flexibility in length.
Since the Unbounded_String type is private, relevant constructor and selector
operations are provided.

        1.a   Reason:  The transformation operations for fixed- and
        bounded-length strings that are not necessarily length preserving are
        supplied for Unbounded_String as procedures as well as functions.
        This allows an implementation to do an initial allocation for an
        unbounded string and to avoid further allocations as long as the
        length does not exceed the allocated length.


                              Static Semantics

2   The library package Strings.Unbounded has the following declaration:

3   with Ada.Strings.Maps;
    package Ada.Strings.Unbounded is
       pragma Preelaborate(Unbounded);

4      type Unbounded_String is private;

5      Null_Unbounded_String : constant Unbounded_String;

6      function Length (Source : in Unbounded_String) return Natural;

7      type String_Access is access all String;
       procedure Free (X : in out String_Access);

8   -- Conversion, Concatenation, and Selection functions

9      function To_Unbounded_String (Source : in String)
          return Unbounded_String;

10     function To_Unbounded_String (Length : in Natural)
          return Unbounded_String;

11     function To_String (Source : in Unbounded_String) return String;

12     procedure Append (Source   : in out Unbounded_String;
                         New_Item : in Unbounded_String);

13     procedure Append (Source   : in out Unbounded_String;
                         New_Item : in String);

14     procedure Append (Source   : in out Unbounded_String;
                         New_Item : in Character);

15     function "&" (Left, Right : in Unbounded_String)
          return Unbounded_String;

16     function "&" (Left : in Unbounded_String; Right : in String)
          return Unbounded_String;

17     function "&" (Left : in String; Right : in Unbounded_String)
          return Unbounded_String;

18     function "&" (Left : in Unbounded_String; Right : in Character)
          return Unbounded_String;

19     function "&" (Left : in Character; Right : in Unbounded_String)
          return Unbounded_String;

20     function Element (Source : in Unbounded_String;
                         Index  : in Positive)
          return Character;

21     procedure Replace_Element (Source : in out Unbounded_String;
                                  Index  : in Positive;
                                  By     : in Character);

22     function Slice (Source : in Unbounded_String;
                       Low    : in Positive;
                       High   : in Natural)
          return String;

23     function "="  (Left, Right : in Unbounded_String) return Boolean;

24     function "="  (Left : in Unbounded_String; Right : in String)
         return Boolean;

25     function "="  (Left : in String; Right : in Unbounded_String)
         return Boolean;

26     function "<"  (Left, Right : in Unbounded_String) return Boolean;

27     function "<"  (Left : in Unbounded_String; Right : in String)
         return Boolean;

28     function "<"  (Left : in String; Right : in Unbounded_String)
         return Boolean;

29     function "<=" (Left, Right : in Unbounded_String) return Boolean;

30     function "<="  (Left : in Unbounded_String; Right : in String)
         return Boolean;

31     function "<="  (Left : in String; Right : in Unbounded_String)
         return Boolean;

32     function ">"  (Left, Right : in Unbounded_String) return Boolean;

33     function ">"  (Left : in Unbounded_String; Right : in String)
         return Boolean;

34     function ">"  (Left : in String; Right : in Unbounded_String)
         return Boolean;

35     function ">=" (Left, Right : in Unbounded_String) return Boolean;

36     function ">="  (Left : in Unbounded_String; Right : in String)
         return Boolean;

37     function ">="  (Left : in String; Right : in Unbounded_String)
         return Boolean;

38  -- Search subprograms

39     function Index (Source   : in Unbounded_String;
                       Pattern  : in String;
                       Going    : in Direction := Forward;
                       Mapping  : in Maps.Character_Mapping
                                    := Maps.Identity)
          return Natural;

40     function Index (Source   : in Unbounded_String;
                       Pattern  : in String;
                       Going    : in Direction := Forward;
                       Mapping  : in Maps.Character_Mapping_Function)
          return Natural;

41     function Index (Source : in Unbounded_String;
                       Set    : in Maps.Character_Set;
                       Test   : in Membership := Inside;
                       Going  : in Direction  := Forward) return Natural;

42     function Index_Non_Blank (Source : in Unbounded_String;
                                 Going  : in Direction := Forward)
          return Natural;

43     function Count (Source   : in Unbounded_String;
                       Pattern  : in String;
                       Mapping  : in Maps.Character_Mapping
                                    := Maps.Identity)
          return Natural;

44     function Count (Source   : in Unbounded_String;
                       Pattern  : in String;
                       Mapping  : in Maps.Character_Mapping_Function)
          return Natural;

45     function Count (Source   : in Unbounded_String;
                       Set      : in Maps.Character_Set)
          return Natural;

46     procedure Find_Token (Source : in Unbounded_String;
                             Set    : in Maps.Character_Set;
                             Test   : in Membership;
                             First  : out Positive;
                             Last   : out Natural);

47  -- String translation subprograms

48     function Translate (Source  : in Unbounded_String;
                           Mapping : in Maps.Character_Mapping)
          return Unbounded_String;

49     procedure Translate (Source  : in out Unbounded_String;
                            Mapping : in Maps.Character_Mapping);

50     function Translate (Source  : in Unbounded_String;
                           Mapping : in Maps.Character_Mapping_Function)
          return Unbounded_String;

51     procedure Translate (Source  : in out Unbounded_String;
                            Mapping : in Maps.Character_Mapping_Function);

52  -- String transformation subprograms

53     function Replace_Slice (Source   : in Unbounded_String;
                               Low      : in Positive;
                               High     : in Natural;
                               By       : in String)
          return Unbounded_String;

54     procedure Replace_Slice (Source   : in out Unbounded_String;
                                Low      : in Positive;
                                High     : in Natural;
                                By       : in String);

55     function Insert (Source   : in Unbounded_String;
                        Before   : in Positive;
                        New_Item : in String)
          return Unbounded_String;

56     procedure Insert (Source   : in out Unbounded_String;
                         Before   : in Positive;
                         New_Item : in String);

57     function Overwrite (Source    : in Unbounded_String;
                           Position  : in Positive;
                           New_Item  : in String)
          return Unbounded_String;

58     procedure Overwrite (Source    : in out Unbounded_String;
                            Position  : in Positive;
                            New_Item  : in String);

59     function Delete (Source  : in Unbounded_String;
                        From    : in Positive;
                        Through : in Natural)
          return Unbounded_String;

60     procedure Delete (Source  : in out Unbounded_String;
                         From    : in Positive;
                         Through : in Natural);

61     function Trim (Source : in Unbounded_String;
                      Side   : in Trim_End)
          return Unbounded_String;

62     procedure Trim (Source : in out Unbounded_String;
                       Side   : in Trim_End);

63     function Trim (Source : in Unbounded_String;
                      Left   : in Maps.Character_Set;
                      Right  : in Maps.Character_Set)
          return Unbounded_String;

64     procedure Trim (Source : in out Unbounded_String;
                       Left   : in Maps.Character_Set;
                       Right  : in Maps.Character_Set);

65     function Head (Source : in Unbounded_String;
                      Count  : in Natural;
                      Pad    : in Character := Space)
          return Unbounded_String;

66     procedure Head (Source : in out Unbounded_String;
                       Count  : in Natural;
                       Pad    : in Character := Space);

67     function Tail (Source : in Unbounded_String;
                      Count  : in Natural;
                      Pad    : in Character := Space)
          return Unbounded_String;

68     procedure Tail (Source : in out Unbounded_String;
                       Count  : in Natural;
                       Pad    : in Character := Space);

69     function "*" (Left  : in Natural;
                     Right : in Character)
          return Unbounded_String;

70     function "*" (Left  : in Natural;
                     Right : in String)
          return Unbounded_String;

71     function "*" (Left  : in Natural;
                     Right : in Unbounded_String)
          return Unbounded_String;

72  private
       ... -- not specified by the language
    end Ada.Strings.Unbounded;

{94-4528.a} {94-4811.a} {94-4884.a} {94-4606.a}

73   Null_Unbounded_String represents the null String.  If an object of type
Unbounded_String is not otherwise initialized, it will be initialized to the
same value as Null_Unbounded_String.

74   The function Length returns the length of the String represented by
Source.

75   The type String_Access provides a (non-private) access type for explicit
processing of unbounded-length strings.  The procedure Free performs an
unchecked deallocation of an object of type String_Access.

76   The function To_Unbounded_String(Source : in String) returns an
Unbounded_String that represents Source.  The function To_Unbounded_
String(Length : in Natural) returns an Unbounded_String that represents an
uninitialized String whose length is Length.

77   The function To_String returns the String with lower bound 1 represented
by Source.  To_String and To_Unbounded_String are related as follows:

   78  If S is a String, then To_String(To_Unbounded_String(S)) = S.

   79  If U is an Unbounded_String, then To_Unbounded_String(To_
       String(U)) = U.

80   For each of the Append procedures, the resulting string represented by
the Source parameter is given by the concatenation of the original value of
Source and the value of New_Item.

81   Each of the "&" functions returns an Unbounded_String obtained by
concatenating the string or character given or represented by one of the
parameters, with the string or character given or represented by the other
parameter, and applying To_Unbounded_String to the concatenation result
string.

82   The Element, Replace_Element, and Slice subprograms have the same effect
as the corresponding bounded-length string subprograms.

83   Each of the functions "=", "<", ">","<=", and ">=" returns the same
result as the corresponding String operation applied to the String values
given or represented by Left and Right.

84   Each of the search subprograms (Index, Index_Non_Blank, Count, Find_
Token) has the same effect as the corresponding subprogram in Strings.Fixed
applied to the string represented by the Unbounded_String parameter.

85   The Translate function has an analogous effect to the corresponding
subprogram in Strings.Fixed.  The translation is applied to the string
represented by the Unbounded_String parameter, and the result is converted
(via To_Unbounded_String) to an Unbounded_String.

86   Each of the transformation functions (Replace_Slice, Insert, Overwrite,
Delete), selector functions (Trim, Head, Tail), and constructor functions
("*") is likewise analogous to its corresponding subprogram in Strings.Fixed.
For each of the subprograms, the corresponding fixed-length string subprogram
is applied to the string represented by the Unbounded_String parameter, and
To_Unbounded_String is applied the result string.

87   For each of the procedures Translate, Replace_Slice, Insert, Overwrite,
Delete, Trim, Head, and Tail, the resulting string represented by the Source
parameter is given by the corresponding function for fixed-length strings
applied to the string represented by Source's original value.


                         Implementation Requirements

88   No storage associated with an Unbounded_String object shall be lost upon
assignment or scope exit.

        88.a   Implementation Note:  A sample implementation of the private
        part of the package and several of the subprograms appears in the
        Rationale.



A.4.6 String-Handling Sets and Mappings

1   The language-defined package Strings.Maps.Constants declares Character_
Set and Character_Mapping constants corresponding to classification and
conversion functions in package Characters.Handling.

        1.a   Discussion:  The Constants package is a child of Strings.Maps
        since it needs visibility of the private part of Strings.Maps in
        order to initialize the constants in a preelaborable way (i.e. via
        aggregates versus function calls).

{94-4469.a} {94-4884.a}


                              Static Semantics

2   The library package Strings.Maps.Constants has the following declaration:

3   package Ada.Strings.Maps.Constants is
       pragma Preelaborate(Constants);

4      Control_Set           : constant Character_Set;
       Graphic_Set           : constant Character_Set;
       Letter_Set            : constant Character_Set;
       Lower_Set             : constant Character_Set;
       Upper_Set             : constant Character_Set;
       Basic_Set             : constant Character_Set;
       Decimal_Digit_Set     : constant Character_Set;
       Hexadecimal_Digit_Set : constant Character_Set;
       Alphanumeric_Set      : constant Character_Set;
       Special_Set           : constant Character_Set;
       ISO_646_Set           : constant Character_Set;

5      Lower_Case_Map        : constant Character_Mapping;
         --Maps to lower case for letters, else identity
       Upper_Case_Map        : constant Character_Mapping;
         --Maps to upper case for letters, else identity
       Basic_Map             : constant Character_Mapping;
         --Maps to basic letter for letters, else identity
6   private
       ... -- not specified by the language
    end Ada.Strings.Maps.Constants;

{94-4469.a}

7   Each of these constants represents a correspondingly named set of
characters or character mapping in Characters.Handling (see A.3.2).



A.4.7 Wide_String Handling

1   Facilities for handling strings of Wide_Character elements are found in
the packages Strings.Wide_Maps, Strings.Wide_Fixed, Strings.Wide_Bounded,
Strings.Wide_Unbounded, and Strings.Wide_Maps.Wide_Constants.  {94-4469.a}
They provide the same string-handling operations as the corresponding
packages for strings of Character elements.  {Ada.Strings.Wide_Fixed}
{Ada.Strings.Wide_Bounded} {Ada.Strings.Wide_Unbounded} {Ada.Strings.Wide_
Maps.Wide_Constants}


                              Static Semantics

2   The package Strings.Wide_Maps has the following declaration.

3   package Ada.Strings.Wide_Maps is
       pragma Preelaborate(Wide_Maps);

4      -- Representation for a set of Wide_Character values:
       type Wide_Character_Set is private;

5      Null_Set : constant Wide_Character_Set;

6      type Wide_Character_Range is
         record
             Low  : Wide_Character;
             High : Wide_Character;
         end record;
       -- Represents Wide_Character range Low..High

7      type Wide_Character_Ranges is array (Positive range <>) of Wide_Characte\
r_Range;

8      function To_Set    (Ranges : in Wide_Character_Ranges) return Wide_Chara\
cter_Set;

9      function To_Set    (Span   : in Wide_Character_Range)  return Wide_Chara\
cter_Set;

10     function To_Ranges (Set    : in Wide_Character_Set)    return Wide_Chara\
cter_Ranges;

11     function "="   (Left, Right : in Wide_Character_Set) return Boolean;

12     function "not" (Right : in Wide_Character_Set)       return Wide_Charact\
er_Set;
       function "and" (Left, Right : in Wide_Character_Set) return Wide_Charact\
er_Set;
       function "or"  (Left, Right : in Wide_Character_Set) return Wide_Charact\
er_Set;
       function "xor" (Left, Right : in Wide_Character_Set) return Wide_Charact\
er_Set;
       function "-"   (Left, Right : in Wide_Character_Set) return Wide_Charact\
er_Set;

13     function Is_In (Element : in Wide_Character;
                       Set     : in Wide_Character_Set)
          return Boolean;

14     function Is_Subset (Elements : in Wide_Character_Set;
                           Set      : in Wide_Character_Set)
          return Boolean;

15     function "<=" (Left  : in Wide_Character_Set;
                      Right : in Wide_Character_Set)
          return Boolean renames Is_Subset;

16     -- Alternative representation for a set of Wide_Character values:
       subtype Wide_Character_Sequence is Wide_String;

17     function To_Set (Sequence  : in Wide_Character_Sequence) return Wide_Cha\
racter_Set;

18     function To_Set (Singleton : in Wide_Character) return Wide_Character_Se\
t;

19     function To_Sequence (Set  : in Wide_Character_Set) return Wide_Characte\
r_Sequence;

20     -- Representation for a Wide_Character to Wide_Character mapping:
       type Wide_Character_Mapping is private;

21     function Value (Map     : in Wide_Character_Mapping;
                       Element : in Wide_Character)
          return Wide_Character;

22     Identity : constant Wide_Character_Mapping;

23     function To_Mapping (From, To : in Wide_Character_Sequence)
          return Wide_Character_Mapping;

24     function To_Domain (Map : in Wide_Character_Mapping)
          return Wide_Character_Sequence;

25     function To_Range  (Map : in Wide_Character_Mapping)
          return Wide_Character_Sequence;

26     type Wide_Character_Mapping_Function is
          access function (From : in Wide_Character) return Wide_Character;

27  private
       ... -- not specified by the language
    end Ada.Strings.Wide_Maps;

{94-4606.a} {94-4465.a} {94-4818.a} {94-4728.a} {94-4913.b}

28   The context clause for each of the packages Strings.Wide_Fixed,
Strings.Wide_Bounded, and Strings.Wide_Unbounded {94-4469.a} identifies
Strings.Wide_Maps instead of Strings.Maps.

29   For each of the packages Strings.Fixed, Strings.Bounded, Strings.-
Unbounded, and Strings.Maps.Constants {94-4469.a} the corresponding wide
string package has the same contents except that

   30  Wide_Space replaces Space

   31  Wide_Character replaces Character

   32  Wide_String replaces String

   33  Wide_Character_Set replaces Character_Set

   34  Wide_Character_Mapping replaces Character_Mapping

   35  Wide_Character_Mapping_Function replaces Character_Mapping_Func-
       tion

   36  Wide_Maps replaces Maps

   37  Bounded_Wide_String replaces Bounded_String

   38  Null_Bounded_Wide_String replaces Null_Bounded_String

   39  To_Bounded_Wide_String replaces To_Bounded_String

   40  To_Wide_String replaces To_String

   41  Unbounded_Wide_String replaces Unbounded_String

   42  Null_Unbounded_Wide_String replaces Null_Unbounded_String

   43  Wide_String_Access replaces String_Access

   44  To_Unbounded_Wide_String replaces To_Unbounded_String

45   The following additional declaration is present in Strings.Wide_
Maps.Wide_Constants:

46  Character_Set : constant Wide_Maps.Wide_Character_Set;
    --Contains each Wide_Character value WC such that Characters.Is_Character(W\
C) is True

{94-4768.s}


     NOTES
47   (12) {Constraint_Error (raised by failure of run-time check)} If a null
     Wide_Character_Mapping_Function is passed to any of the Wide_String
     handling subprograms, Constraint_Error is propagated.

48   (13) Each Wide_Character_Set constant in the package Strings.Wide_
     Maps.Wide_Constants contains no values outside the Character portion of
     Wide_Character.  Similarly, each Wide_Character_Mapping constant in this
     package is the identity mapping when applied to any element outside the
     Character portion of Wide_Character.



A.5 The Numerics Packages

1   The library package Numerics is the parent of several child units that
provide facilities for mathematical computation.  One child, the generic
package Generic_Elementary_Functions, is defined in A.5.1, together with
nongeneric equivalents; two others, the package Float_Random and the generic
package Discrete_Random, are defined in A.5.2.  Additional (optional)
children are defined in Annex G, ``Numerics''.


                              Static Semantics

2

3   package Ada.Numerics is
       pragma Pure(Numerics);
       Argument_Error : exception;
       Pi : constant :=
              3.14159_26535_89793_23846_26433_83279_50288_41971_69399_37511;
       e  : constant :=
              2.71828_18284_59045_23536_02874_71352_66249_77572_47093_69996;
    end Ada.Numerics;

4   The Argument_Error exception is raised by a subprogram in a child unit of
Numerics to signal that one or more of the actual subprogram parameters are
outside the domain of the corresponding mathematical function.


                         Implementation Permissions

5   The implementation may specify the values of Pi and e to a larger number
of significant digits.
        5.a   Reason:  51 digits seem more than adequate for all present
        computers; converted to binary, the values given above are accurate
        to more than 160 bits.  Nevertheless, the permission allows
        implementations to accommodate unforeseen hardware advances.


                            Extensions to Ada 83

        5.b   {extensions to Ada 83} Numerics and its children were not
        predefined in Ada 83.



A.5.1 Elementary Functions

1   Implementation-defined approximations to the mathematical functions known
as the ``elementary functions'' are provided by the subprograms in
Numerics.Generic_Elementary_Functions.  Nongeneric equivalents of this
generic package for each of the predefined floating point types are also
provided as children of Numerics.

        1.a   Implementation defined:  The accuracy actually achieved by the
        elementary functions.


                              Static Semantics

2   The generic library package Numerics.Generic_Elementary_Functions has the
following declaration:

3   generic
       type Float_Type is digits <>;
    package Ada.Numerics.Generic_Elementary_Functions is
       pragma Pure(Generic_Elementary_Functions);

4      function Sqrt    (X           : Float_Type'Base)        return Float_Typ\
e'Base;
       function Log     (X           : Float_Type'Base)        return Float_Typ\
e'Base;
       function Log     (X, Base     : Float_Type'Base)        return Float_Typ\
e'Base;
       function Exp     (X           : Float_Type'Base)        return Float_Typ\
e'Base;
       function "**"    (Left, Right : Float_Type'Base)        return Float_Typ\
e'Base;

5      function Sin     (X           : Float_Type'Base)        return Float_Typ\
e'Base;
       function Sin     (X, Cycle    : Float_Type'Base)        return Float_Typ\
e'Base;
       function Cos     (X           : Float_Type'Base)        return Float_Typ\
e'Base;
       function Cos     (X, Cycle    : Float_Type'Base)        return Float_Typ\
e'Base;
       function Tan     (X           : Float_Type'Base)        return Float_Typ\
e'Base;
       function Tan     (X, Cycle    : Float_Type'Base)        return Float_Typ\
e'Base;
       function Cot     (X           : Float_Type'Base)        return Float_Typ\
e'Base;
       function Cot     (X, Cycle    : Float_Type'Base)        return Float_Typ\
e'Base;

6      function Arcsin  (X           : Float_Type'Base)        return Float_Typ\
e'Base;
       function Arcsin  (X, Cycle    : Float_Type'Base)        return Float_Typ\
e'Base;
       function Arccos  (X           : Float_Type'Base)        return Float_Typ\
e'Base;
       function Arccos  (X, Cycle    : Float_Type'Base)        return Float_Typ\
e'Base;
       function Arctan  (Y           : Float_Type'Base;
                         X           : Float_Type'Base := 1.0) return Float_Typ\
e'Base;
       function Arctan  (Y           : Float_Type'Base;
                         X           : Float_Type'Base := 1.0;
                         Cycle       : Float_Type'Base)        return Float_Typ\
e'Base;
       function Arccot  (X           : Float_Type'Base;
                         Y           : Float_Type'Base := 1.0) return Float_Typ\
e'Base;
       function Arccot  (X           : Float_Type'Base;
                         Y           : Float_Type'Base := 1.0;
                         Cycle       : Float_Type'Base)        return Float_Typ\
e'Base;

7      function Sinh    (X           : Float_Type'Base)        return Float_Typ\
e'Base;
       function Cosh    (X           : Float_Type'Base)        return Float_Typ\
e'Base;
       function Tanh    (X           : Float_Type'Base)        return Float_Typ\
e'Base;
       function Coth    (X           : Float_Type'Base)        return Float_Typ\
e'Base;
       function Arcsinh (X           : Float_Type'Base)        return Float_Typ\
e'Base;
       function Arccosh (X           : Float_Type'Base)        return Float_Typ\
e'Base;
       function Arctanh (X           : Float_Type'Base)        return Float_Typ\
e'Base;
       function Arccoth (X           : Float_Type'Base)        return Float_Typ\
e'Base;

8   end Ada.Numerics.Generic_Elementary_Functions;

9   {Ada.Numerics.Elementary_Functions} The library package Numerics.-
Elementary_Functions defines the same subprograms as Numerics.Generic_
Elementary_Functions, except that the predefined type Float is systematically
substituted for Float_Type'Base throughout.  Nongeneric equivalents of
Numerics.Generic_Elementary_Functions for each of the other predefined
floating point types are defined similarly, with the names Numerics.Short_
Elementary_Functions, Numerics.Long_Elementary_Functions, etc.

        9.a   Reason:  The nongeneric equivalents are provided to allow the
        programmer to construct simple mathematical applications without
        being required to understand and use generics.

10   The functions have their usual mathematical meanings.  When the Base
parameter is specified, the Log function computes the logarithm to the given
base; otherwise, it computes the natural logarithm.  When the Cycle parameter
is specified, the parameter X of the forward trigonometric functions (Sin,
Cos, Tan, and Cot) and the results of the inverse trigonometric functions
(Arcsin, Arccos, Arctan, and Arccot) are measured in units such that a full
cycle of revolution has the given value; otherwise, they are measured in
radians.

11   The computed results of the mathematically multivalued functions are
rendered single-valued by the following conventions, which are meant to imply
the principal branch:

   12  The results of the Sqrt and Arccosh functions and that of the
       exponentiation operator are nonnegative.

   13  The result of the Arcsin function is in the quadrant containing
       the point (1.0, x), where x is the value of the parameter X. This
       quadrant is I or IV; thus, the range of the Arcsin function is
       approximately -Pi/2.0 to Pi/2.0 (-Cycle/4.0 to Cycle/4.0, if the
       parameter Cycle is specified).

   14  The result of the Arccos function is in the quadrant containing
       the point (x, 1.0), where x is the value of the parameter X. This
       quadrant is I or II; thus, the Arccos function ranges from 0.0 to
       approximately Pi (Cycle/2.0, if the parameter Cycle is
       specified).

   15  The results of the Arctan and Arccot functions are in the
       quadrant containing the point (x, y), where x and y are the
       values of the parameters X and Y, respectively.  This may be any
       quadrant (I through IV) when the parameter X (resp., Y) of Arctan
       (resp., Arccot) is specified, but it is restricted to quadrants I
       and IV (resp., I and II) when that parameter is omitted.  Thus,
       the range when that parameter is specified is approximately -Pi
       to Pi (-Cycle/2.0 to Cycle/2.0, if the parameter Cycle is
       specified); when omitted, the range of Arctan (resp., Arccot) is
       that of Arcsin (resp., Arccos), as given above.  When the point
       (x, y) lies on the negative x-axis, the result approximates

          16  Pi (resp., -Pi) when the sign of the parameter Y is
              positive (resp., negative), if Float_Type'Signed_Zeros is
              True;

          17  Pi, if Float_Type'Signed_Zeros is False.

18   (In the case of the inverse trigonometric functions, in which a result
lying on or near one of the axes may not be exactly representable, the
approximation inherent in computing the result may place it in an adjacent
quadrant, close to but on the wrong side of the axis.)


                              Dynamic Semantics

19   The exception Numerics.Argument_Error is raised, signaling a parameter
value outside the domain of the corresponding mathematical function, in the
following cases:

   20  by any forward or inverse trigonometric function with specified
       cycle, when the value of the parameter Cycle is zero or negative;

   21  by the Log function with specified base, when the value of the
       parameter Base is zero, one, or negative;

   22  by the Sqrt and Log functions, when the value of the parameter X
       is negative;

   23  by the exponentiation operator, when the value of the left
       operand is negative or when both operands have the value zero;

   24  by the Arcsin, Arccos, and Arctanh functions, when the absolute
       value of the parameter X exceeds one;

   25  by the Arctan and Arccot functions, when the parameters X and Y
       both have the value zero;

   26  by the Arccosh function, when the value of the parameter X is
       less than one; and

   27  by the Arccoth function, when the absolute value of the parameter
       X is less than one.

28   {Division_Check [partial]} {check, language-defined (Division_Check)}
{Constraint_Error (raised by failure of run-time check)} The exception
Constraint_Error is raised, signaling a pole of the mathematical function
(analogous to dividing by zero), in the following cases, provided that Float_
Type'Machine_Overflows is True:

   29  by the Log, Cot, and Coth functions, when the value of the
       parameter X is zero;

   30  by the exponentiation operator, when the value of the left
       operand is zero and the value of the exponent is negative;

   31  by the Tan function with specified cycle, when the value of the
       parameter X is an odd multiple of the quarter cycle;

   32  by the Cot function with specified cycle, when the value of the
       parameter X is zero or a multiple of the half cycle; and

   33  by the Arctanh and Arccoth functions, when the absolute value of
       the parameter X is one.

34   {Constraint_Error (raised by failure of run-time check)}[Constraint_
Error can also be raised when a finite result overflows (see G.2.4); this may
occur for parameter values sufficiently near poles, and, in the case of some
of the functions, for parameter values with sufficiently large magnitudes.]

        34.a   Reason:  The purpose of raising Constraint_Error (rather than
        Numerics.Argument_Error) at the poles of a function, when Float_
        Type'Machine_Overflows is True, is to provide continuous behavior as
        the actual parameters of the function approach the pole and finally
        reach it.

{unspecified [partial]} When Float_Type'Machine_Overflows is False, the
result at poles is unspecified.

        34.b   Discussion:  It is anticipated that an Ada binding to IEC
        559:1989 will be developed in the future.  As part of such a binding,
        the Machine_Overflows attribute of a conformant floating point type
        will be specified to yield False, which will permit both the
        predefined arithmetic operations and implementations of the
        elementary functions to deliver signed infinities (and set the
        overflow flag defined by the binding) instead of raising Constraint_
        Error in overflow situations, when traps are disabled.  Similarly, it
        is appropriate for the elementary functions to deliver signed
        infinities (and set the zero-divide flag defined by the binding)
        instead of raising Constraint_Error at poles, when traps are
        disabled.  Finally, such a binding should also specify the behavior
        of the elementary functions, when sensible, given parameters with
        infinite values.

35   When one parameter of a function with multiple parameters represents a
pole and another is outside the function's domain, the latter takes
precedence (i.e., Numerics.Argument_Error is raised).


                         Implementation Requirements

36   In the implementation of Numerics.Generic_Elementary_Functions, the
range of intermediate values allowed during the calculation of a final result
shall not be affected by any range constraint of the subtype Float_Type.

        36.a   Implementation Note:  Implementations of Numerics.Generic_
        Elementary_Functions written in Ada should therefore avoid declaring
        local variables of subtype Float_Type; the subtype Float_Type'Base
        should be used instead.

37   {prescribed result (for the evaluation of an elementary function)} In
the following cases, evaluation of an elementary function shall yield the
prescribed result, provided that the preceding rules do not call for an
exception to be raised:

   38  When the parameter X has the value zero, the Sqrt, Sin, Arcsin,
       Tan, Sinh, Arcsinh, Tanh, and Arctanh functions yield a result of
       zero, and the Exp, Cos, and Cosh functions yield a result of one.

   39  When the parameter X has the value one, the Sqrt function yields
       a result of one, and the Log, Arccos, and Arccosh functions yield
       a result of zero.

   40  When the parameter Y has the value zero and the parameter X has a
       positive value, the Arctan and Arccot functions yield a result of
       zero.

   41  The results of the Sin, Cos, Tan, and Cot functions with
       specified cycle are exact when the mathematical result is zero;
       those of the first two are also exact when the mathematical
       result is +/-1.0.

   42  Exponentiation by a zero exponent yields the value one.
       Exponentiation by a unit exponent yields the value of the left
       operand.  Exponentiation of the value one yields the value one.
       Exponentiation of the value zero yields the value zero.

43   Other accuracy requirements for the elementary functions, which apply
only in implementations conforming to the Numerics Annex, and then only in
the ``strict'' mode defined there (see G.2), are given in G.2.4.

44   When Float_Type'Signed_Zeros is True, the sign of a zero result shall be
as follows:

   45  A prescribed zero result delivered at the origin by one of the
       odd functions (Sin, Arcsin, Sinh, Arcsinh, Tan, Arctan or Arccot
       as a function of Y when X is fixed and positive, Tanh, and
       Arctanh) has the sign of the parameter X (Y, in the case of
       Arctan or Arccot).

   46  A prescribed zero result delivered by one of the odd functions
       away from the origin, or by some other elementary function, has
       an implementation-defined sign.

 46.a   Implementation defined:  The sign of a zero result from some of
        the operators or functions in Numerics.Generic_Elementary_
        Functions, when Float_Type'Signed_Zeros is True.

   47  [A zero result that is not a prescribed result (i.e., one that
       results from rounding or underflow) has the correct mathematical
       sign.

 47.a   Reason:  This is a consequence of the rules specified in IEC
        559:1989 as they apply to underflow situations with traps
        disabled.

       ]


                         Implementation Permissions

48   The nongeneric equivalent packages may, but need not, be actual
instantiations of the generic package for the appropriate predefined type.


                         Wording Changes From Ada 83

        48.a   The semantics of Numerics.Generic_Elementary_Functions differs
        from Generic_Elementary_Functions as defined in ISO/IEC DIS 11430
        (for Ada 83) in the following ways:

         48.b  The generic package is a child unit of the package
               defining the Argument_Error exception.

         48.c  DIS 11430 specified names for the nongeneric equivalents,
               if provided.  Here, those nongeneric equivalents are
               required.

         48.d  Implementations are not allowed to impose an optional
               restriction that the generic actual parameter associated
               with Float_Type be unconstrained.  (In view of the
               ability to declare variables of subtype Float_Type'Base
               in implementations of Numerics.Generic_Elementary_Func-
               tions, this flexibility is no longer needed.)

         48.e  The sign of a prescribed zero result at the origin of the
               odd functions is specified, when Float_Type'Signed_Zeros
               is True.  This conforms with recommendations of Kahan and
               other numerical analysts.

         48.f  The dependence of Arctan and Arccot on the sign of a
               parameter value of zero is tied to the value of Float_
               Type'Signed_Zeros.

         48.g  Sqrt is prescribed to yield a result of one when its
               parameter has the value one.  This guarantee makes it
               easier to achieve certain prescribed results of the
               complex elementary functions (see G.1.2, ``Complex
               Elementary Functions'').

         48.h  Conformance to accuracy requirements is conditional.



A.5.2 Random Number Generation

1   [Facilities for the generation of pseudo-random floating point numbers
are provided in the package Numerics.Float_Random; the generic package
Numerics.Discrete_Random provides similar facilities for the generation of
pseudo-random integers and pseudo-random values of enumeration types.
{random number} For brevity, pseudo-random values of any of these types are
called random numbers.

2   Some of the facilities provided are basic to all applications of random
numbers.  These include a limited private type each of whose objects serves
as the generator of a (possibly distinct) sequence of random numbers; a
function to obtain the ``next'' random number from a given sequence of random
numbers (that is, from its generator); and subprograms to initialize or
reinitialize a given generator to a time-dependent state or a state denoted
by a single integer.

3   Other facilities are provided specifically for advanced applications.
These include subprograms to save and restore the state of a given generator;
a private type whose objects can be used to hold the saved state of a
generator; and subprograms to obtain a string representation of a given
generator state, or, given such a string representation, the corresponding
state.]

        3.a   Discussion:  These facilities support a variety of requirements
        ranging from repeatable sequences (for debugging) to unique sequences
        in each execution of a program.


                              Static Semantics

4   The library package Numerics.Float_Random has the following declaration:

5   package Ada.Numerics.Float_Random is

6      -- Basic facilities

7      type Generator is limited private;

8      subtype Uniformly_Distributed is Float range 0.0 .. 1.0;
       function Random (Gen : Generator) return Uniformly_Distributed;

9      procedure Reset (Gen       : in Generator;
                        Initiator : in Integer);
       procedure Reset (Gen       : in Generator);

10     -- Advanced facilities

11     type State is private;

12     procedure Save  (Gen        : in  Generator;
                        To_State   : out State);
       procedure Reset (Gen        : in  Generator;
                        From_State : in  State);

13     Max_Image_Width : constant := implementation-defined integer value;

14     function Image (Of_State    : State)  return String;
       function Value (Coded_State : String) return State;
15  private
       ... -- not specified by the language
    end Ada.Numerics.Float_Random;

16   The generic library package Numerics.Discrete_Random has the following
declaration:

17  generic
       type Result_Subtype is (<>);
    package Ada.Numerics.Discrete_Random is

18     -- Basic facilities

19     type Generator is limited private;

20     function Random (Gen : Generator) return Result_Subtype;

21     procedure Reset (Gen       : in Generator;
                        Initiator : in Integer);
       procedure Reset (Gen       : in Generator);

22     -- Advanced facilities

23     type State is private;

24     procedure Save  (Gen        : in  Generator;
                        To_State   : out State);
       procedure Reset (Gen        : in  Generator;
                        From_State : in  State);

25     Max_Image_Width : constant := implementation-defined integer value;

26     function Image (Of_State    : State)  return String;
       function Value (Coded_State : String) return State;

27  private
       ... -- not specified by the language
    end Ada.Numerics.Discrete_Random;

        27.a   Implementation defined:  The value of Numerics.Float_
        Random.Max_Image_Width.

        27.b   Implementation defined:  The value of Numerics.Discrete_
        Random.Max_Image_Width.

        27.c   Implementation Note:  The following is a possible
        implementation of the private part of each package (assuming the
        presence of ``with Ada.Finalization;'' as a context clause):

27.d        type State is ...;
            type Access_State is access State;
            type Generator is new Finalization.Limited_Controlled with
               record
                  S : Access_State := new State'(...);
               end record;
            procedure Finalize (G : in out Generator);

        27.e   Clearly some level of indirection is required in the
        implementation of a Generator, since the parameter mode is in for all
        operations on a Generator.  For this reason, Numerics.Float_Random
        and Numerics.Discrete_Random cannot be declared pure.

28   An object of the limited private type Generator is associated with a
sequence of random numbers.  Each generator has a hidden (internal) state,
which the operations on generators use to determine the position in the
associated sequence.  {unspecified [partial]} All generators are implicitly
initialized to an unspecified state that does not vary from one program
execution to another; they may also be explicitly initialized, or
reinitialized, to a time-dependent state, to a previously saved state, or to
a state uniquely denoted by an integer value.

        28.a   Discussion:  The repeatability provided by the implicit
        initialization may be exploited for testing or debugging purposes.

29   An object of the private type State can be used to hold the internal
state of a generator.  Such objects are only needed if the application is
designed to save and restore generator states or to examine or manufacture
them.

30   The operations on generators affect the state and therefore the future
values of the associated sequence.  The semantics of the operations on
generators and states are defined below.


31  function Random (Gen : Generator) return Uniformly_Distributed;
    function Random (Gen : Generator) return Result_Subtype;

        32   Obtains the ``next'' random number from the given generator,
        relative to its current state, according to an implementation-defined
        algorithm.  The result of the function in Numerics.Float_Random is
        delivered as a value of the subtype Uniformly_Distributed, which is a
        subtype of the predefined type Float having a range of 0.0 .. 1.0.
        The result of the function in an instantiation of Numerics.Discrete_
        Random is delivered as a value of the generic formal subtype Result_
        Subtype.

        32.a   Implementation defined:  The algorithms for random number
        generation.

        32.b   Reason:  The requirement for a level of indirection in
        accessing the internal state of a generator arises from the desire to
        make Random a function, rather than a procedure.


33  procedure Reset (Gen       : in Generator;
                     Initiator : in Integer);
    procedure Reset (Gen       : in Generator);

        34   {unspecified [partial]} Sets the state of the specified
        generator to one that is an unspecified function of the value of the
        parameter Initiator (or to a time-dependent state, if only a
        generator parameter is specified).  {Time-dependent Reset procedure
        (of the random number generator)} The latter form of the procedure is
        known as the time-dependent Reset procedure.

        34.a   Implementation Note:  The time-dependent Reset procedure can
        be implemented by mapping the current time and date as determined by
        the system clock into a state, but other implementations are
        possible.  For example, a white-noise generator or a radioactive
        source can be used to generate time-dependent states.


35  procedure Save  (Gen        : in  Generator;
                     To_State   : out State);
    procedure Reset (Gen        : in  Generator;
                     From_State : in  State);

        36   Save obtains the current state of a generator.  Reset gives a
        generator the specified state.  A generator that is reset to a state
        previously obtained by invoking Save is restored to the state it had
        when Save was invoked.


37  function Image (Of_State    : State)  return String;
    function Value (Coded_State : String) return State;

        38   Image provides a representation of a state coded (in an
        implementation-defined way) as a string whose length is bounded by
        the value of Max_Image_Width.  Value is the inverse of Image:
        Value(Image(S)) = S for each state S that can be obtained from a
        generator by invoking Save.

        38.a   Implementation defined:  The string representation of a random
        number generator's state.


                              Dynamic Semantics

39   {Range_Check [partial]} {check, language-defined (Range_Check)}
{Constraint_Error (raised by failure of run-time check)} Instantiation of
Numerics.Discrete_Random with a subtype having a null range raises
Constraint_Error.

40   {Range_Check [partial]} {check, language-defined (Range_Check)}
{Constraint_Error (raised by failure of run-time check)} Invoking Value with
a string that is not the image of any generator state raises Constraint_
Error.


                         Implementation Requirements

41   A sufficiently long sequence of random numbers obtained by successive
calls to Random is approximately uniformly distributed over the range of the
result subtype.

42   The Random function in an instantiation of Numerics.Discrete_Random is
guaranteed to yield each value in its result subtype in a finite number of
                                                                15
calls, provided that the number of such values does not exceed 2  .

43   Other performance requirements for the random number generator, which
apply only in implementations conforming to the Numerics Annex, and then only
in the ``strict'' mode defined there (see G.2), are given in G.2.5.


                         Documentation Requirements

44   {documentation requirements} No one algorithm for random number
generation is best for all applications.  To enable the user to determine the
suitability of the random number generators for the intended application, the
implementation shall describe the algorithm used and shall give its period,
if known exactly, or a lower bound on the period, if the exact period is
unknown.  Periods that are so long that the periodicity is unobservable in
practice can be described in such terms, without giving a numerical bound.

45   The implementation also shall document the minimum time interval between
calls to the time-dependent Reset procedure that are guaranteed to initiate
different sequences, and it shall document the nature of the strings that
Value will accept without raising Constraint_Error.

        45.a   Implementation defined:  The minimum time interval between
        calls to the time-dependent Reset procedure that are guaranteed to
        initiate different random number sequences.


                            Implementation Advice

46   Any storage associated with an object of type Generator should be
reclaimed on exit from the scope of the object.
        46.a   Ramification:  A level of indirection is implicit in the
        semantics of the operations, given that they all take parameters of
        mode in.  This implies that the full type of Generator probably
        should be a controlled type, with appropriate finalization to reclaim
        any heap-allocated storage.

47   If the generator period is sufficiently long in relation to the number
of distinct initiator values, then each possible value of Initiator passed to
Reset should initiate a sequence of random numbers that does not, in a
practical sense, overlap the sequence initiated by any other value.  If this
is not possible, then the mapping between initiator values and generator
states should be a rapidly varying function of the initiator value.


     NOTES
48   (14) If two or more tasks are to share the same generator, then the
     tasks have to synchronize their access to the generator as for any
     shared variable (see 9.10).

49   (15) Within a given implementation, a repeatable random number sequence
     can be obtained by relying on the implicit initialization of generators
     or by explicitly initializing a generator with a repeatable initiator
     value.  Different sequences of random numbers can be obtained from a
     given generator in different program executions by explicitly
     initializing the generator to a time-dependent state.

50   (16) A given implementation of the Random function in Numerics.Float_
     Random may or may not be capable of delivering the values 0.0 or 1.0.
     Portable applications should assume that these values, or values
     sufficiently close to them to behave indistinguishably from them, can
     occur.  If a sequence of random integers from some fixed range is
     needed, the application should use the Random function in an appropriate
     instantiation of Numerics.Discrete_Random, rather than transforming the
     result of the Random function in Numerics.Float_Random.  However, some
     applications with unusual requirements, such as for a sequence of random
     integers each drawn from a different range, will find it more convenient
     to transform the result of the floating point Random function.  For
     M>=1, the expression

51       Integer(Float(M) * Random(G)) mod M

     52   transforms the result of Random(G) to an integer uniformly
     distributed over the range 0 .. M-1; it is valid even if Random delivers
     0.0 or 1.0.  Each value of the result range is possible, provided that M
     is not too large.  Exponentially distributed (floating point) random
     numbers with mean and standard deviation 1.0 can be obtained by the
     transformation

53       -Log(Random(G) + Float'Model_Small))

     54   where Log comes from Numerics.Elementary_Functions (see A.5.1); in
     this expression, the addition of Float'Model_Small avoids the exception
     that would be raised were Log to be given the value zero, without
     affecting the result (in most implementations) when Random returns a
     nonzero value.


                                  Examples

55   Example of a program that plays a simulated dice game:

56  with Ada.Numerics.Discrete_Random;
    procedure Dice_Game is
       subtype Die is Integer range 1 .. 6;
       subtype Dice is Integer range 2*Die'First .. 2*Die'Last;
       package Random_Die is new Ada.Numerics.Discrete_Random (Die);
       use Random_Die;
       G : Generator;
       D : Dice;
    begin
       Reset (G);  -- Start the generator in a unique state in each run
       loop
          -- Roll a pair of dice; sum and process the results
          D := Random(G) + Random(G);
          ...
       end loop;
    end Dice_Game;

57   Example of a program that simulates coin tosses:

58  with Ada.Numerics.Discrete_Random;
    procedure Flip_A_Coin is
       type Coin is (Heads, Tails);
       package Random_Coin is new Ada.Numerics.Discrete_Random (Coin);
       use Random_Coin;
       G : Generator;
    begin
       Reset (G);  -- Start the generator in a unique state in each run
       loop
          -- Toss a coin and process the result
          case Random(G) is
              when Heads =>
                 ...
              when Tails =>
                 ...
          end case;
       ...
       end loop;
    end Flip_A_Coin;

59   Example of a parallel simulation of a physical system, with a separate
generator of event probabilities in each task:

60  with Ada.Numerics.Float_Random;
    procedure Parallel_Simulation is
       use Ada.Numerics.Float_Random;
       task type Worker is
          entry Initialize_Generator (Initiator : in Integer);
          ...
       end Worker;
       W : array (1 .. 10) of Worker;
       task body Worker is
          G : Generator;
          Probability_Of_Event : Uniformly_Distributed;
       begin
          accept Initialize_Generator (Initiator : in Integer) do
             Reset (G, Initiator);
          end Initialize_Generator;
          loop
             ...
             Probability_Of_Event := Random(G);
             ...
          end loop;
       end Worker;
    begin
       -- Initialize the generators in the Worker tasks to different states
       for I in W'Range loop
          W(I).Initialize_Generator (I);
       end loop;
       ... -- Wait for the Worker tasks to terminate
    end Parallel_Simulation;


     NOTES
61   (17) Notes on the last example:  Although each Worker task initializes
     its generator to a different state, those states will be the same in
     every execution of the program.  The generator states can be initialized
     uniquely in each program execution by instantiating Ada.Numerics.-
     Discrete_Random for the type Integer in the main procedure, resetting
     the generator obtained from that instance to a time-dependent state, and
     then using random integers obtained from that generator to initialize
     the generators in each Worker task.



A.5.3 Attributes of Floating Point Types

                              Static Semantics

1   {representation-oriented attributes (of a floating point subtype)} The
following representation-oriented attributes are defined for every subtype S
of a floating point type T.

2   S'Machine_Radix
                Yields the radix of the hardware representation of the type
                T.  The value of this attribute is of the type universal_
                integer.

3   {canonical form} The values of other representation-oriented attributes
of a floating point subtype, and of the ``primitive function'' attributes of
a floating point subtype described later, are defined in terms of a
particular representation of nonzero values called the canonical form.  The
canonical form (for the type T) is the form

                               exponent
    +/-mantissa*T'Machine_Radix

where

    4  mantissa is a fraction in the number base T'Machine_Radix, the
       first digit of which is nonzero, and

    5  exponent is an integer.

6   S'Machine_Mantissa
                Yields the largest value of p such that every value
                expressible in the canonical form (for the type T), having a
                p-digit mantissa and an exponent between T'Machine_Emin and
                T'Machine_Emax, is a machine number (see 3.5.7) of the type
                T.  This attribute yields a value of the type universal_
                integer.

6.a     Ramification:  Values of a type held in an extended register are, in
        general, not machine numbers of the type, since they cannot be
        expressed in the canonical form with a sufficiently short mantissa.

7   S'Machine_Emin
                Yields the smallest (most negative) value of exponent such
                that every value expressible in the canonical form (for the
                type T), having a mantissa of T'Machine_Mantissa digits, is a
                machine number (see 3.5.7) of the type T.  This attribute
                yields a value of the type universal_integer.

8   S'Machine_Emax
                Yields the largest (most positive) value of exponent such
                that every value expressible in the canonical form (for the
                type T), having a mantissa of T'Machine_Mantissa digits, is a
                machine number (see 3.5.7) of the type T.  This attribute
                yields a value of the type universal_integer.
8.a     Ramification:  Note that the above definitions do not determine
        unique values for the representation-oriented attributes of floating
        point types.  The implementation may choose any set of values that
        collectively satisfies the definitions.  {94-4737.b} {94-4889.c}

9   S'Denorm
                Yields the value True if every value expressible in the form

                                               T'Machine_Emin
                    +/-mantissa*T'Machine_Radix

                where mantissa is a nonzero T'Machine_Mantissa-digit fraction
                in the number base T'Machine_Radix, the first digit of which
                is zero, is a machine number (see 3.5.7) of the type T;
                yields the value False otherwise.  The value of this
                attribute is of the predefined type Boolean.

10   {denormalized number} The values described by the formula in the
definition of S'Denorm are called denormalized numbers.  {normalized number}
A nonzero machine number that is not a denormalized number is a normalized
number.

        10.a   Discussion:  The intent is that S'Denorm be True when such
        denormalized numbers exist and are generated in the circumstances
        defined by IEC 559:1989, though the latter requirement is not
        formalized here.

{represented in canonical form} {canonical-form representation} A normalized
number x of a given type T is said to be represented in canonical form when
it is expressed in the canonical form (for the type T) with a mantissa having
T'Machine_Mantissa digits; the resulting form is the canonical-form
representation of x.

11  S'Machine_Rounds
                Yields the value True if rounding is performed on inexact
                results of every predefined operation that yields a result of
                the type T; yields the value False otherwise.  The value of
                this attribute is of the predefined type Boolean.

11.a    Discussion:  It is difficult to be more precise about what it means
        to round the result of a predefined operation.  If the implementation
        does not use extended registers, so that every arithmetic result is
        necessarily a machine number, then rounding seems to imply two
        things:

         11.b  S'Model_Mantissa = S'Machine_Mantissa, so that operand
               preperturbation never occurs;

         11.c  when the exact mathematical result is not a machine
               number, the result of a predefined operation must be the
               nearer of the two adjacent machine numbers.

11.d    Technically, this attribute should yield False when extended
        registers are used, since a few computed results will cross over the
        half-way point as a result of double rounding, if and when a value
        held in an extended register has to be reduced in precision to that
        of the machine numbers.  It does not seem desirable to preclude the
        use of extended registers when S'Machine_Rounds could otherwise be
        True.

12  S'Machine_Overflows
                Yields the value True if overflow and divide-by-zero are
                detected and reported by raising Constraint_Error for every
                predefined operation that yields a result of the type T;
                yields the value False otherwise.  The value of this
                attribute is of the predefined type Boolean.

13  S'Signed_Zeros
                Yields the value True if the hardware representation for the
                type T has the capability of representing both positively and
                negatively signed zeros, these being generated and used by
                the predefined operations of the type T as specified in IEC
                559:1989; yields the value False otherwise.  The value of
                this attribute is of the predefined type Boolean.

14   {normalized exponent} For every value x of a floating point type T, the
normalized exponent of x is defined as follows:

   15  the normalized exponent of zero is (by convention) zero;

   16  for nonzero x, the normalized exponent of x is the unique integer
                                  k-1                     k
       k such that T'Machine_Radix   <=|x|<T'Machine_Radix .

        16.a   Ramification:  The normalized exponent of a normalized number
        x is the value of exponent in the canonical-form representation of x.

        16.b   The normalized exponent of a denormalized number is less than
        the value of T'Machine_Emin.

17   {primitive function} The following primitive function attributes are
defined for any subtype S of a floating point type T.

18  S'Exponent
                S'Exponent denotes a function with the following specifica-
                tion:

19                  function S'Exponent (X : T)
                      return universal_integer

                20   The function yields the normalized exponent of X.

21  S'Fraction
                S'Fraction denotes a function with the following specifica-
                tion:

22                  function S'Fraction (X : T)
                      return T

                                                                    -k
                23   The function yields the value X*T'Machine_Radix  , where
                k is the normalized exponent of X.  A zero result[, which can
                only occur when X is zero,] has the sign of X.

23.a    Discussion:  Informally, when X is a normalized number, the result is
        the value obtained by replacing the exponent by zero in the
        canonical-form representation of X.

23.b    Ramification:  Except when X is zero, the magnitude of the result is
        greater than or equal to the reciprocal of T'Machine_Radix and less
        than one; consequently, the result is always a normalized number,
        even when X is a denormalized number.

23.c    Implementation Note:  When X is a denormalized number, the result is
        the value obtained by replacing the exponent by zero in the
        canonical-form representation of the result of scaling X up
        sufficiently to normalize it.

24  S'Compose
                S'Compose denotes a function with the following specifica-
                tion:

25                  function S'Compose (Fraction : T;
                                        Exponent : universal_integer)
                      return T

                26   {Constraint_Error (raised by failure of run-time check)}
                                                           Exponent-k
                Let v be the value Fraction*T'Machine_Radix          , where
                k is the normalized exponent of Fraction.  If v is a machine
                number of the type T, or if |v|>=T'Model_Small, the function
                yields v; otherwise, it yields either one of the machine
                numbers of the type T adjacent to v.  {Range_Check [partial]}
                {check, language-defined (Range_Check)} Constraint_Error is
                optionally raised if v is outside the base range of S. A zero
                result has the sign of Fraction when S'Signed_Zeros is True.

26.a    Discussion:  Informally, when Fraction and v are both normalized
        numbers, the result is the value obtained by replacing the exponent
        by Exponent in the canonical-form representation of Fraction.

26.b    Ramification:  If Exponent is less than T'Machine_Emin and Fraction
        is nonzero, the result is either zero, T'Model_Small, or (if T'Denorm
        is True) a denormalized number.

27  S'Scaling
                S'Scaling denotes a function with the following specifica-
                tion:

28                  function S'Scaling (X : T;
                                        Adjustment : universal_integer)
                      return T

                29   {Constraint_Error (raised by failure of run-time check)}
                                                    Adjustment
                Let v be the value X*T'Machine_Radix          .  If v is a
                machine number of the type T, or if |v|>=T'Model_Small, the
                function yields v; otherwise, it yields either one of the
                machine numbers of the type T adjacent to v.  {Range_Check
                [partial]} {check, language-defined (Range_Check)}
                Constraint_Error is optionally raised if v is outside the
                base range of S. A zero result has the sign of X when
                S'Signed_Zeros is True.

29.a    Discussion:  Informally, when X and v are both normalized numbers,
        the result is the value obtained by increasing the exponent by
        Adjustment in the canonical-form representation of X.

29.b    Ramification:  If Adjustment is sufficiently small (i.e.,
        sufficiently negative), the result is either zero, T'Model_Small, or
        (if T'Denorm is True) a denormalized number.

30  S'Floor
                S'Floor denotes a function with the following specification:

31                  function S'Floor (X : T)
                      return T

                32   The function yields the value Floor(X), i.e., the
                largest (most positive) integral value less than or equal to
                X.  When X is zero, the result has the sign of X; a zero
                result otherwise has a positive sign.  {94-4630.e}
                {94-4889.m} {94-4983.a}

33  S'Ceiling
                S'Ceiling denotes a function with the following specifica-
                tion:

34                  function S'Ceiling (X : T)
                      return T

                35   The function yields the value Ceiling(X), i.e., the
                smallest (most negative) integral value greater than or equal
                to X.  When X is zero, the result has the sign of X; a zero
                result otherwise has a negative sign when S'Signed_Zeros is
                True.  {94-4630.f} {94-4889.m} {94-4983.b}

36  S'Rounding
                S'Rounding denotes a function with the following specifica-
                tion:

37                  function S'Rounding (X : T)
                      return T

                38   The function yields the integral value nearest to X,
                rounding away from zero if X lies exactly halfway between two
                integers.  A zero result has the sign of X when S'Signed_
                Zeros is True.

39  S'Unbiased_Rounding
                S'Unbiased_Rounding denotes a function with the following
                specification:

40                  function S'Unbiased_Rounding (X : T)
                      return T

                41   The function yields the integral value nearest to X,
                rounding toward the even integer if X lies exactly halfway
                between two integers.  A zero result has the sign of X when
                S'Signed_Zeros is True.

42  S'Truncation
                S'Truncation denotes a function with the following
                specification:

43                  function S'Truncation (X : T)
                      return T

                44   The function yields the value Ceiling(X) when X is
                negative, and Floor(X) otherwise.  A zero result has the sign
                of X when S'Signed_Zeros is True.

45  S'Remainder
                S'Remainder denotes a function with the following
                specification:

46                  function S'Remainder (X, Y : T)
                      return T

                47   {Constraint_Error (raised by failure of run-time check)}
                For nonzero Y, let v be the value X-n*Y, where n is the
                integer nearest to the exact value of X/Y; if |n-X/Y|=1/2,
                then n is chosen to be even.  If v is a machine number of the
                type T, the function yields v; otherwise, it yields zero.
                {Division_Check [partial]} {check, language-defined
                (Division_Check)} Constraint_Error is raised if Y is zero.  A
                zero result has the sign of X when S'Signed_Zeros is True.

47.a    Ramification:  The magnitude of the result is less than or equal to
        one-half the magnitude of Y.

47.b    Discussion:  Given machine numbers X and Y of the type T, v is
        necessarily a machine number of the type T, except when Y is in the
        neighborhood of zero, X is sufficiently close to a multiple of Y, and
        T'Denorm is False.

48  S'Adjacent
                S'Adjacent denotes a function with the following specifica-
                tion:

49                  function S'Adjacent (X, Towards : T)
                      return T

                50   {Constraint_Error (raised by failure of run-time check)}
                If Towards=X, the function yields X; otherwise, it yields the
                machine number of the type T adjacent to X in the direction
                of Towards, if that machine number exists.  {Range_Check
                [partial]} {check, language-defined (Range_Check)} If the
                result would be outside the base range of S, Constraint_Error
                is raised.  When T'Signed_Zeros is True, a zero result has
                the sign of X.  When Towards is zero, its sign has no bearing
                on the result.

50.a    Ramification:  The value of S'Adjacent(0.0, 1.0) is the smallest
        normalized positive number of the type T when T'Denorm is False and
        the smallest denormalized positive number of the type T when T'Denorm
        is True.

51  S'Copy_Sign
                S'Copy_Sign denotes a function with the following
                specification:

52                  function S'Copy_Sign (Value, Sign : T)
                      return T

                53   {Constraint_Error (raised by failure of run-time check)}
                If the value of Value is nonzero, the function yields a
                result whose magnitude is that of Value and whose sign is
                that of Sign; otherwise, it yields the value zero.  {Range_
                Check [partial]} {check, language-defined (Range_Check)}
                Constraint_Error is optionally raised if the result is
                outside the base range of S. A zero result has the sign of
                Sign when S'Signed_Zeros is True.

53.a    Discussion:  S'Copy_Sign is provided for convenience in restoring the
        sign to a quantity from which it has been temporarily removed, or to
        a related quantity.  When S'Signed_Zeros is True, it is also
        instrumental in determining the sign of a zero quantity, when
        required.  (Because negative and positive zeros compare equal in
        systems conforming to IEC 559:1989, a negative zero does not appear
        to be negative when compared to zero.)  The sign determination is
        accomplished by transferring the sign of the zero quantity to a
        nonzero quantity and then testing for a negative result.

54  S'Leading_Part
                S'Leading_Part denotes a function with the following
                specification:

55                  function S'Leading_Part (X : T;
                                             Radix_Digits : universal_integer)
                      return T

                                                       k-Radix_Digits
                56   Let v be the value T'Machine_Radix              , where
                k is the normalized exponent of X.  The function yields the
                value

                   57  Floor(X/v)*v, when X is nonnegative and Radix_
                       Digits is positive;

                   58  Ceiling(X/v)*v, when X is negative and Radix_
                       Digits is positive.

                59   {Constraint_Error (raised by failure of run-time check)}
                {Range_Check [partial]} {check, language-defined (Range_
                Check)} Constraint_Error is raised when Radix_Digits is zero
                or negative.  A zero result[, which can only occur when X is
                zero,] has the sign of X.

59.a    Discussion:  Informally, if X is nonzero, the result is the value
        obtained by retaining only the specified number of (leading)
        significant digits of X (in the machine radix), setting all other
        digits to zero.

59.b    Implementation Note:  The result can be obtained by first scaling X
        up, if necessary to normalize it, then masking the mantissa so as to
        retain only the specified number of leading digits, then scaling the
        result back down if X was scaled up.

60  S'Machine
                S'Machine denotes a function with the following specifica-
                tion:

61                  function S'Machine (X : T)
                      return T

                62   {Constraint_Error (raised by failure of run-time check)}
                If X is a machine number of the type T, the function yields
                X; otherwise, it yields the value obtained by rounding or
                truncating X to either one of the adjacent machine numbers of
                the type T.  {Range_Check [partial]} {check, language-defined
                (Range_Check)} Constraint_Error is raised if rounding or
                truncating X to the precision of the machine numbers results
                in a value outside the base range of S. A zero result has the
                sign of X when S'Signed_Zeros is True.

62.a    Discussion:  All of the primitive function attributes except Rounding
        and Machine correspond to subprograms in the Generic_Primitive_
        Functions generic package proposed as a separate ISO standard
        (ISO/IEC DIS 11729) for Ada 83.  The Scaling, Unbiased_Rounding, and
        Truncation attributes correspond to the Scale, Round, and Truncate
        functions, respectively, in Generic_Primitive_Functions.  The
        Rounding attribute rounds away from zero; this functionality was not
        provided in Generic_Primitive_Functions.  The name Round was not
        available for either of the primitive function attributes that
        perform rounding, since an attribute of that name is used for a
        different purpose for decimal fixed point types.  Likewise, the name
        Scale was not available, since an attribute of that name is also used
        for a different purpose for decimal fixed point types.  The
        functionality of the Machine attribute was also not provided in
        Generic_Primitive_Functions.  The functionality of the Decompose
        procedure of Generic_Primitive_Functions is only provided in the form
        of the separate attributes Exponent and Fraction.  The functionality
        of the Successor and Predecessor functions of Generic_Primitive_
        Functions is provided by the extension of the existing Succ and Pred
        attributes.

62.b    Implementation Note:  The primitive function attributes may be
        implemented either with appropriate floating point arithmetic
        operations or with integer and logical operations that act on parts
        of the representation directly.  The latter is strongly encouraged
        when it is more efficient than the former; it is mandatory when the
        former cannot deliver the required accuracy due to limitations of the
        implementation's arithmetic operations.

63   {model-oriented attributes (of a floating point subtype)} The following
model-oriented attributes are defined for any subtype S of a floating point
type T.
64  S'Model_Mantissa
                If the Numerics Annex is not supported, this attribute yields
                an implementation defined value that is greater than or equal
                to Ceiling(d*log (10)/log (T'Machine_Radix))+1, where d is
                the requested decimal precision of T, and less than or equal
                to the value of T'Machine_Mantissa.  See G.2.2 for further
                requirements that apply to implementations supporting the
                Numerics Annex.  The value of this attribute is of the type
                universal_integer.  {94-4587.a} {94-4889.h}

65  S'Model_Emin
                If the Numerics Annex is not supported, this attribute yields
                an implementation defined value that is greater than or equal
                to the value of T'Machine_Emin.  See G.2.2 for further
                requirements that apply to implementations supporting the
                Numerics Annex.  The value of this attribute is of the type
                universal_integer.  {94-4587.a} {94-4889.h}

66  S'Model_Epsilon
                                                1-T'Model_Mantissa
                Yields the value T'Machine_Radix                  .  The
                value of this attribute is of the type universal_real.

66.a    Discussion:  In most implementations, this attribute yields the
        absolute value of the difference between one and the smallest machine
        number of the type T above one which, when added to one, yields a
        machine number different from one.  Further discussion can be found
        in G.2.2.

67  S'Model_Small
                                                T'Model_Emin-1
                Yields the value T'Machine_Radix              .  The value of
                this attribute is of the type universal_real.

67.a    Discussion:  In most implementations, this attribute yields the
        smallest positive normalized number of the type T, i.e. the number
        corresponding to the positive underflow threshold.  In some
        implementations employing a radix-complement representation for the
        type T, the positive underflow threshold is closer to zero than is
        the negative underflow threshold, with the consequence that the
        smallest positive normalized number does not coincide with the
        positive underflow threshold (i.e., it exceeds the latter).  Further
        discussion can be found in G.2.2.

68  S'Model
                S'Model denotes a function with the following specification:

69                  function S'Model (X : T)
                      return T

                70   If the Numerics Annex is not supported, the meaning of
                this attribute is implementation defined; see G.2.2 for the
                definition that applies to implementations supporting the
                Numerics Annex.  {94-4587.a} {94-4889.h}

71  S'Safe_First
                Yields the lower bound of the safe range (see 3.5.7) of the
                type T.  If the Numerics Annex is not supported, the value of
                this attribute is implementation defined; see G.2.2 for the
                definition that applies to implementations supporting the
                Numerics Annex.  The value of this attribute is of the type
                universal_real.

72  S'Safe_Last
                Yields the upper bound of the safe range (see 3.5.7) of the
                type T.  If the Numerics Annex is not supported, the value of
                this attribute is implementation defined; see G.2.2 for the
                definition that applies to implementations supporting the
                Numerics Annex.  The value of this attribute is of the type
                universal_real.

72.a    Discussion:  A predefined floating point arithmetic operation that
        yields a value in the safe range of its result type is guaranteed not
        to overflow.

72.b    To be honest:  An exception is made for exponentiation by a negative
        exponent in 4.5.6.

72.c    Implementation defined:  The values of the Model_Mantissa, Model_
        Emin, Model_Epsilon, Model, Safe_First, and Safe_Last attributes, if
        the Numerics Annex is not supported.


                        Incompatibilities With Ada 83

        72.d   {incompatibilities with Ada 83} The Epsilon and Mantissa
        attributes of floating point types are removed from the language and
        replaced by Model_Epsilon and Model_Mantissa, which may have
        different values (as a result of changes in the definition of model
        numbers); the replacement of one set of attributes by another is
        intended to convert what would be an inconsistent change into an
        incompatible change.

        72.e   The Emax, Small, Large, Safe_Emax, Safe_Small, and Safe_Large
        attributes of floating point types are removed from the language.
        Small and Safe_Small are collectively replaced by Model_Small, which
        is functionally equivalent to Safe_Small, though it may have a
        slightly different value.  The others are collectively replaced by
        Safe_First and Safe_Last.  Safe_Last is functionally equivalent to
        Safe_Large, though it may have a different value; Safe_First is
        comparable to the negation of Safe_Large but may differ slightly from
        it as well as from the negation of Safe_Last.  Emax and Safe_Emax had
        relatively few uses in Ada 83; T'Safe_Emax can be computed in the
        revised language as Integer'Min(T'Exponent(T'Safe_First),
        T'Exponent(T'Safe_Last)).

        72.f   Implementations are encouraged to eliminate the incom-
        patibilities discussed here by retaining the old attributes, during a
        transition period, in the form of implementation-defined attributes
        with their former values.

                            Extensions to Ada 83

        72.g   {extensions to Ada 83} The Model_Emin attribute is new.  It is
        conceptually similar to the negation of Safe_Emax attribute of Ada
        83, adjusted for the fact that the model numbers now have the
        hardware radix.  It is a fundamental determinant, along with Model_
        Mantissa, of the set of model numbers of a type (see G.2.1).

        72.h   The Denorm and Signed_Zeros attributes are new, as are all of
        the primitive function attributes.



A.5.4 Attributes of Fixed Point Types

                              Static Semantics

1   {representation-oriented attributes (of a fixed point subtype)} The
following representation-oriented attributes are defined for every subtype S
of a fixed point type T.

2   S'Machine_Radix
                Yields the radix of the hardware representation of the type
                T.  The value of this attribute is of the type universal_
                integer.

3   S'Machine_Rounds
                Yields the value True if rounding is performed on inexact
                results of every predefined operation that yields a result of
                the type T; yields the value False otherwise.  The value of
                this attribute is of the predefined type Boolean.

4   S'Machine_Overflows
                Yields the value True if overflow and divide-by-zero are
                detected and reported by raising Constraint_Error for every
                predefined operation that yields a result of the type T;
                yields the value False otherwise.  The value of this
                attribute is of the predefined type Boolean.


                        Incompatibilities With Ada 83

        4.a   {incompatibilities with Ada 83} The Mantissa, Large, Safe_
        Small, and Safe_Large attributes of fixed point types are removed
        from the language.

        4.b   Implementations are encouraged to eliminate the resulting
        incompatibility by retaining these attributes, during a transition
        period, in the form of implementation-defined attributes with their
        former values.

                            Extensions to Ada 83

        4.c   {extensions to Ada 83} The Machine_Radix attribute is now
        allowed for fixed point types.  It is also specifiable in an
        attribute definition clause (see F.1).



A.6 Input-Output

1   [{input} {output} Input-output is provided through language-defined
packages, each of which is a child of the root package Ada.  The generic
packages Sequential_IO and Direct_IO define input-output operations
applicable to files containing elements of a given type.  The generic package
Storage_IO supports reading from and writing to an in-memory buffer.
Additional operations for text input-output are supplied in the packages
Text_IO and Wide_Text_IO.  Heterogeneous input-output is provided through the
child packages Streams.Stream_IO and Text_IO.Text_Streams (see also 13.13).
The package IO_Exceptions defines the exceptions needed by the predefined
input-output packages.]


                         Inconsistencies With Ada 83

        1.a   {inconsistencies with Ada 83} The introduction of Append_File
        as a new element of the enumeration type File_Mode in Sequential_IO
        and Text_IO, and the introduction of several new declarations in
        Text_IO, may result in name clashes in the presence of use clauses.

                            Extensions to Ada 83

        1.b   {extensions to Ada 83} Text_IO enhancements (Get_Immediate,
        Look_Ahead, Standard_Error, Modular_IO, Decimal_IO), Wide_Text_IO,
        and the stream input-output facilities are new in Ada 9X.

                         Wording Changes From Ada 83
        1.c   RM83-14.6, "Low Level Input-Output," is removed.  This has no
        semantic effect, since the package was entirely implementation
        defined, nobody actually implemented it, and if they did, they can
        always provide it as a vendor-supplied package.



A.7 External Files and File Objects

                              Static Semantics

1   {external file} {name (of an external file)} {form (of an external file)}
Values input from the external environment of the program, or output to the
external environment, are considered to occupy external files.  {94-4845.a}
An external file can be anything external to the program that can produce a
value to be read or receive a value to be written.  An external file is
identified by a string (the name).  A second string (the form) gives further
system-dependent characteristics that may be associated with the file, such
as the physical organization or access rights.  The conventions governing the
interpretation of such strings shall be documented.

2   {file (as file object)} Input and output operations are expressed as
operations on objects of some file type, rather than directly in terms of the
external files.  In the remainder of this section, the term file is always
used to refer to a file object; the term external file is used otherwise.

3   Input-output for sequential files of values of a single element type is
defined by means of the generic package Sequential_IO.  In order to define
sequential input-output for a given element type, an instantiation of this
generic unit, with the given type as actual parameter, has to be declared.
The resulting package contains the declaration of a file type (called File_
Type) for files of such elements, as well as the operations applicable to
these files, such as the Open, Read, and Write procedures.

4   Input-output for direct access files is likewise defined by a generic
package called Direct_IO.  Input-output in human-readable form is defined by
the (nongeneric) packages Text_IO for Character and String data, and Wide_
Text_IO for Wide_Character and Wide_String data.  Input-output for files
containing streams of elements representing values of possibly different
types is defined by means of the (nongeneric) package Streams.Stream_IO.

5   Before input or output operations can be performed on a file, the file
first has to be associated with an external file.  While such an association
is in effect, the file is said to be open, and otherwise the file is said to
be closed.

6   The language does not define what happens to external files after the
completion of the main program and all the library tasks (in particular, if
corresponding files have not been closed).  {access types (input-output
unspecified)} {input-output (unspecified for access types)} {unspecified
[partial]} The effect of input-output for access types is unspecified.

7   {current mode (of an open file)} An open file has a current mode, which
is a value of one of the following enumeration types:


8   type File_Mode is (In_File, Inout_File, Out_File);  --  for Direct_IO

        9   These values correspond respectively to the cases where only
        reading, both reading and writing, or only writing are to be
        performed.


10  type File_Mode is (In_File, Out_File, Append_File);
    --  for Sequential_IO, Text_IO, Wide_Text_IO, and Stream_IO

        11   These values correspond respectively to the cases where only
        reading, only writing, or only appending are to be performed.
        12   The mode of a file can be changed.

13   Several file management operations are common to Sequential_IO,
Direct_IO, Text_IO, and Wide_Text_IO.  These operations are described in
subclause A.8.2 for sequential and direct files.  Any additional effects
concerning text input-output are described in subclause A.10.2.

14   The exceptions that can be propagated by the execution of an
input-output subprogram are defined in the package IO_Exceptions; the
situations in which they can be propagated are described following the
description of the subprogram (and in clause A.13).  {Storage_Error (raised
by failure of run-time check)} {Program_Error (raised by failure of run-time
check)} The exceptions Storage_Error and Program_Error may be propagated.
(Program_Error can only be propagated due to errors made by the caller of the
subprogram.)  Finally, exceptions can be propagated in certain
implementation-defined situations.

        14.a   Implementation defined:  Any implementation-defined charac-
        teristics of the input-output packages.


     NOTES
15   (18) Each instantiation of the generic packages Sequential_IO and
     Direct_IO declares a different type File_Type.  In the case of Text_IO,
     Wide_Text_IO, and Streams.Stream_IO, the corresponding type File_Type is
     unique.

16   (19) A bidirectional device can often be modeled as two sequential files
     associated with the device, one of mode In_File, and one of mode Out_
     File.  An implementation may restrict the number of files that may be
     associated with a given external file.



A.8 Sequential and Direct Files

                              Static Semantics

1   {sequential file} {direct file} Two kinds of access to external files are
defined in this subclause:  sequential access and direct access.  The
corresponding file types and the associated operations are provided by the
generic packages Sequential_IO and Direct_IO. A file object to be used for
sequential access is called a sequential file, and one to be used for direct
access is called a direct file.  Access to stream files is described in
A.12.1.

2   {sequential access} For sequential access, the file is viewed as a
sequence of values that are transferred in the order of their appearance (as
produced by the program or by the external environment).  {94-4845.a} When
the file is opened with mode In_File or Out_File, transfer starts
respectively from or to the beginning of the file.  When the file is opened
with mode Append_File, transfer to the file starts after the last element of
the file.

        2.a   Discussion:  Adding stream I/O necessitates a review of the
        terminology.  In Ada 83, `sequential' implies both the access method
        (purely sequential -- that is, no indexing or positional access) and
        homogeneity.  Direct access includes purely sequential access and
        indexed access, as well as homogeneity.  In Ada 9X, streams allow
        purely sequential access but also positional access to an individual
        element, and are heterogeneous.  We considered generalizing the
        notion of `sequential file' to include both Sequential_IO and
        Stream_IO files, but since streams allow positional access it seems
        misleading to call them sequential files.  Or, looked at differently,
        if the criterion for calling something a sequential file is whether
        it permits (versus requires) purely sequential access, then one could
        just as soon regard a Direct_IO file as a sequential file.

        2.b   It seems better to regard `sequential file' as meaning `only
        permitting purely sequential access'; hence we have decided to
        supplement `sequential access' and `direct access' with a third
        category, informally called `access to streams'.  (We decided against
        the term `stream access' because of possible confusion with the
        Stream_Access type declared in one of the stream packages.)

3   {direct access} {index (of an element of an open direct file)} {current
size (of an external file)} For direct access, the file is viewed as a set of
elements occupying consecutive positions in linear order; a value can be
transferred to or from an element of the file at any selected position.  The
position of an element is specified by its index, which is a number, greater
than zero, of the implementation-defined integer type Count.  The first
element, if any, has index one; the index of the last element, if any, is
called the current size; the current size is zero if there are no elements.
The current size is a property of the external file.

4   {current index (of an open direct file)} An open direct file has a
current index, which is the index that will be used by the next read or write
operation.  When a direct file is opened, the current index is set to one.
The current index of a direct file is a property of a file object, not of an
external file.



A.8.1 The Generic Package Sequential_IO

                              Static Semantics

1   The generic library package Sequential_IO has the following declaration:

2   with Ada.IO_Exceptions;
    generic
       type Element_Type(<>) is private;
    package Ada.Sequential_IO is

3      type File_Type is limited private;

4      type File_Mode is (In_File, Out_File, Append_File);

5      -- File management

6      procedure Create(File : in out File_Type;
                        Mode : in File_Mode := Out_File;
                        Name : in String := "";
                        Form : in String := "");

7      procedure Open  (File : in out File_Type;
                        Mode : in File_Mode;
                        Name : in String;
                        Form : in String := "");

8      procedure Close (File : in out File_Type);
       procedure Delete(File : in out File_Type);
       procedure Reset (File : in out File_Type; Mode : in File_Mode);
       procedure Reset (File : in out File_Type);

9      function Mode   (File : in File_Type) return File_Mode;
       function Name   (File : in File_Type) return String;
       function Form   (File : in File_Type) return String;

10     function Is_Open(File : in File_Type) return Boolean;

11     -- Input and output operations
12     procedure Read  (File : in File_Type; Item : out Element_Type);
       procedure Write (File : in File_Type; Item : in Element_Type);

13     function End_Of_File(File : in File_Type) return Boolean;

14     -- Exceptions

15     Status_Error : exception renames IO_Exceptions.Status_Error;
       Mode_Error   : exception renames IO_Exceptions.Mode_Error;
       Name_Error   : exception renames IO_Exceptions.Name_Error;
       Use_Error    : exception renames IO_Exceptions.Use_Error;
       Device_Error : exception renames IO_Exceptions.Device_Error;
       End_Error    : exception renames IO_Exceptions.End_Error;
       Data_Error   : exception renames IO_Exceptions.Data_Error;

16  private
       ... -- not specified by the language
    end Ada.Sequential_IO;


                        Incompatibilities With Ada 83

        16.a   {incompatibilities with Ada 83} The new enumeration element
        Append_File may introduce upward incompatibilities.  It is possible
        that a program based on the assumption that File_Mode'Last = Out_File
        will be illegal (e.g., case statement choice coverage) or execute
        with a different effect in Ada 9X.



A.8.2 File Management

                              Static Semantics

1   The procedures and functions described in this subclause provide for the
control of external files; their declarations are repeated in each of the
packages for sequential, direct, text, and stream input-output.  For text
input-output, the procedures Create, Open, and Reset have additional effects
described in subclause A.10.2.


2   procedure Create(File : in out File_Type;
                     Mode : in File_Mode := default_mode;
                     Name : in String := "";
                     Form : in String := "");

        3   Establishes a new external file, with the given name and form,
        and associates this external file with the given file.  The given
        file is left open.  The current mode of the given file is set to the
        given access mode.  The default access mode is the mode Out_File for
        sequential and text input-output; it is the mode Inout_File for
        direct input-output.  For direct access, the size of the created file
        is implementation defined.
        4   A null string for Name specifies an external file that is not
        accessible after the completion of the main program (a temporary
        file).  A null string for Form specifies the use of the default
        options of the implementation for the external file.
        5   The exception Status_Error is propagated if the given file is
        already open.  The exception Name_Error is propagated if the string
        given as Name does not allow the identification of an external file.
        The exception Use_Error is propagated if, for the specified mode, the
        external environment does not support creation of an external file
        with the given name (in the absence of Name_Error) and form.
        {94-4845.a}


6   procedure Open(File : in out File_Type;
                   Mode : in File_Mode;
                   Name : in String;
                   Form : in String := "");

        7   Associates the given file with an existing external file having
        the given name and form, and sets the current mode of the given file
        to the given mode.  The given file is left open.
        8   The exception Status_Error is propagated if the given file is
        already open.  The exception Name_Error is propagated if the string
        given as Name does not allow the identification of an external file;
        in particular, this exception is propagated if no external file with
        the given name exists.  The exception Use_Error is propagated if, for
        the specified mode, the external environment does not support opening
        for an external file with the given name (in the absence of Name_
        Error) and form.  {94-4845.a}


9   procedure Close(File : in out File_Type);

        10   Severs the association between the given file and its associated
        external file.  The given file is left closed.  In addition, for
        sequential files, if the file being closed has mode Out_File or
        Append_File, then the last element written since the most recent open
        or reset is the last element that can be read from the file.  If no
        elements have been written and the file mode is Out_File, then the
        closed file is empty.  If no elements have been written and the file
        mode is Append_File, then the closed file is unchanged.
        11   The exception Status_Error is propagated if the given file is
        not open.


12  procedure Delete(File : in out File_Type);

        13   Deletes the external file associated with the given file.  The
        given file is closed, and the external file ceases to exist.
        14   The exception Status_Error is propagated if the given file is
        not open.  The exception Use_Error is propagated if deletion of the
        external file is not supported by the external environment.
        {94-4845.a}


15  procedure Reset(File : in out File_Type; Mode : in File_Mode);
    procedure Reset(File : in out File_Type);

        16   Resets the given file so that reading from its elements can be
        restarted from the beginning of the file (for modes In_File and
        Inout_File), and so that writing to its elements can be restarted at
        the beginning of the file (for modes Out_File and Inout_File) or
        after the last element of the file (for mode Append_File).  In
        particular, for direct access this means that the current index is
        set to one.  If a Mode parameter is supplied, the current mode of the
        given file is set to the given mode.  In addition, for sequential
        files, if the given file has mode Out_File or Append_File when Reset
        is called, the last element written since the most recent open or
        reset is the last element that can be read from the file.  If no
        elements have been written and the file mode is Out_File, the reset
        file is empty.  If no elements have been written and the file mode is
        Append_File, then the reset file is unchanged.
        17   The exception Status_Error is propagated if the file is not
        open.  The exception Use_Error is propagated if the external
        environment does not support resetting for the external file and,
        also, if the external environment does not support resetting to the
        specified mode for the external file.  {94-4845.a}


18  function Mode(File : in File_Type) return File_Mode;

        19   Returns the current mode of the given file.
        20   The exception Status_Error is propagated if the file is not
        open.


21  function Name(File : in File_Type) return String;

        22   Returns a string which uniquely identifies the external file
        currently associated with the given file (and may thus be used in an
        Open operation).  If an external environment allows alternative
        specifications of the name (for example, abbreviations), the string
        returned by the function should correspond to a full specification of
        the name.  {94-4845.a}
        23   The exception Status_Error is propagated if the given file is
        not open.  The exception Use_Error is propagated if the associated
        external file is a temporary file that cannot be opened by any name.


24  function Form(File : in File_Type) return String;

        25   Returns the form string for the external file currently
        associated with the given file.  If an external environment allows
        alternative specifications of the form (for example, abbreviations
        using default options), the string returned by the function should
        correspond to a full specification (that is, it should indicate
        explicitly all options selected, including default options).
        {94-4845.a}
        26   The exception Status_Error is propagated if the given file is
        not open.


27  function Is_Open(File : in File_Type) return Boolean;

        28   Returns True if the file is open (that is, if it is associated
        with an external file), otherwise returns False.


                         Implementation Permissions

29   An implementation may propagate Name_Error or Use_Error if an attempt is
made to use an I/O feature that cannot be supported by the implementation due
to limitations in the external environment.  {94-4845.a} Any such restriction
should be documented.



A.8.3 Sequential Input-Output Operations

                              Static Semantics

1   The operations available for sequential input and output are described in
this subclause.  The exception Status_Error is propagated if any of these
operations is attempted for a file that is not open.


2   procedure Read(File : in File_Type; Item : out Element_Type);

        3   Operates on a file of mode In_File.  Reads an element from the
        given file, and returns the value of this element in the Item
        parameter.

        3.a   Discussion:  We considered basing Sequential_IO.Read on
        Element_Type'Read from an implicit stream associated with the
        sequential file.  However, Element_Type'Read is a type-related
        attribute, whereas Sequential_IO should take advantage of the
        particular constraints of the actual subtype corresponding to
        Element_Type to minimize the size of the external file.  Furthermore,
        forcing the implementation of Sequential_IO to be based on Element_
        Type'Read would create an upward incompatibility since existing data
        files written by an Ada 83 program using Sequential_IO might not be
        readable by the identical program built with an Ada 9X implementation
        of Sequential_IO.
        3.b   An Ada 9X implementation might still use an implementation-
        defined attribute analogous to 'Read to implement the procedure Read,
        but that attribute will likely have to be subtype-specific rather
        than type-related, and it need not be user-specifiable.  Such an
        attribute will presumably be needed to implement the generic package
        Storage_IO (see A.9).

        4   The exception Mode_Error is propagated if the mode is not In_
        File.  The exception End_Error is propagated if no more elements can
        be read from the given file.  The exception Data_Error can be
        propagated if the element read cannot be interpreted as a value of
        the subtype Element_Type (see A.13, ``Exceptions in Input-Output'').

        4.a   Discussion:  Data_Error need not be propagated if the check is
        too complex.  See A.13, ``Exceptions in Input-Output''.


5   procedure Write(File : in File_Type; Item : in Element_Type);

        6   Operates on a file of mode Out_File or Append_File.  Writes the
        value of Item to the given file.
        7   The exception Mode_Error is propagated if the mode is not Out_
        File or Append_File.  The exception Use_Error is propagated if the
        capacity of the external file is exceeded.


8   function End_Of_File(File : in File_Type) return Boolean;

        9   Operates on a file of mode In_File.  Returns True if no more
        elements can be read from the given file; otherwise returns False.
        10   The exception Mode_Error is propagated if the mode is not In_
        File.



A.8.4 The Generic Package Direct_IO

                              Static Semantics

1   The generic library package Direct_IO has the following declaration:

2   with Ada.IO_Exceptions;
    generic
       type Element_Type is private;
    package Ada.Direct_IO is

3      type File_Type is limited private;

4      type File_Mode is (In_File, Inout_File, Out_File);
       type Count     is range 0 .. implementation-defined;
       subtype Positive_Count is Count range 1 .. Count'Last;

5      -- File management

6      procedure Create(File : in out File_Type;
                        Mode : in File_Mode := Inout_File;
                        Name : in String := "";
                        Form : in String := "");

7      procedure Open  (File : in out File_Type;
                        Mode : in File_Mode;
                        Name : in String;
                        Form : in String := "");

8      procedure Close (File : in out File_Type);
       procedure Delete(File : in out File_Type);
       procedure Reset (File : in out File_Type; Mode : in File_Mode);
       procedure Reset (File : in out File_Type);

9      function Mode   (File : in File_Type) return File_Mode;
       function Name   (File : in File_Type) return String;
       function Form   (File : in File_Type) return String;

10     function Is_Open(File : in File_Type) return Boolean;

11     -- Input and output operations

12     procedure Read (File : in File_Type; Item : out Element_Type;
                                            From : in Positive_Count);
       procedure Read (File : in File_Type; Item : out Element_Type);

13     procedure Write(File : in File_Type; Item : in  Element_Type;
                                            To   : in Positive_Count);
       procedure Write(File : in File_Type; Item : in Element_Type);

14     procedure Set_Index(File : in File_Type; To : in Positive_Count);

15     function Index(File : in File_Type) return Positive_Count;
       function Size (File : in File_Type) return Count;

16     function End_Of_File(File : in File_Type) return Boolean;

17     -- Exceptions

18     Status_Error : exception renames IO_Exceptions.Status_Error;
       Mode_Error   : exception renames IO_Exceptions.Mode_Error;
       Name_Error   : exception renames IO_Exceptions.Name_Error;
       Use_Error    : exception renames IO_Exceptions.Use_Error;
       Device_Error : exception renames IO_Exceptions.Device_Error;
       End_Error    : exception renames IO_Exceptions.End_Error;
       Data_Error   : exception renames IO_Exceptions.Data_Error;

19  private
       ... -- not specified by the language
    end Ada.Direct_IO;

        19.a   Reason:  The Element_Type formal of Direct_IO does not have an
        unknown_discriminant_part (unlike Sequential_IO) so that the
        implementation can make use of the ability to declare uninitialized
        variables of the type.



A.8.5 Direct Input-Output Operations

                              Static Semantics

1   The operations available for direct input and output are described in
this subclause.  The exception Status_Error is propagated if any of these
operations is attempted for a file that is not open.


2   procedure Read(File : in File_Type; Item : out Element_Type;
                                        From : in  Positive_Count);
    procedure Read(File : in File_Type; Item : out Element_Type);

        3   Operates on a file of mode In_File or Inout_File.  In the case of
        the first form, sets the current index of the given file to the index
        value given by the parameter From.  Then (for both forms) returns, in
        the parameter Item, the value of the element whose position in the
        given file is specified by the current index of the file; finally,
        increases the current index by one.
        4   The exception Mode_Error is propagated if the mode of the given
        file is Out_File.  The exception End_Error is propagated if the index
        to be used exceeds the size of the external file.  The exception
        Data_Error can be propagated if the element read cannot be
        interpreted as a value of the subtype Element_Type (see A.13).
        {94-4768.c}


5   procedure Write(File : in File_Type; Item : in Element_Type;
                                         To   : in Positive_Count);
    procedure Write(File : in File_Type; Item : in Element_Type);

        6   Operates on a file of mode Inout_File or Out_File.  In the case
        of the first form, sets the index of the given file to the index
        value given by the parameter To.  Then (for both forms) gives the
        value of the parameter Item to the element whose position in the
        given file is specified by the current index of the file; finally,
        increases the current index by one.
        7   The exception Mode_Error is propagated if the mode of the given
        file is In_File.  The exception Use_Error is propagated if the
        capacity of the external file is exceeded.


8   procedure Set_Index(File : in File_Type; To : in Positive_Count);

        9   Operates on a file of any mode.  Sets the current index of the
        given file to the given index value (which may exceed the current
        size of the file).


10  function Index(File : in File_Type) return Positive_Count;

        11   Operates on a file of any mode.  Returns the current index of
        the given file.


12  function Size(File : in File_Type) return Count;

        13   Operates on a file of any mode.  Returns the current size of the
        external file that is associated with the given file.


14  function End_Of_File(File : in File_Type) return Boolean;

        15   Operates on a file of mode In_File or Inout_File.  Returns True
        if the current index exceeds the size of the external file; otherwise
        returns False.
        16   The exception Mode_Error is propagated if the mode of the given
        file is Out_File.


     NOTES
17   (20) Append_File mode is not supported for the generic package
     Direct_IO.



A.9 The Generic Package Storage_IO

1   The generic package Storage_IO provides for reading from and writing to
an in-memory buffer.  This generic package supports the construction of
user-defined input-output packages.
        1.a   Reason:  This package exists to allow the portable construction
        of user-defined direct-access-oriented input-output packages.  The
        Write procedure writes a value of type Element_Type into a Storage_
        Array of size Buffer_Size, flattening out any implicit levels of
        indirection used in the representation of the type.  The Read
        procedure reads a value of type Element_Type from the buffer,
        reconstructing any implicit levels of indirection used in the
        representation of the type.  It also properly initializes any type
        tags that appear within the value, presuming that the buffer was
        written by a different program and that tag values for the``same''
        type might vary from one executable to another.


                              Static Semantics

2   The generic library package Storage_IO has the following declaration:

3   with Ada.IO_Exceptions;
    with System.Storage_Elements;
    generic
       type Element_Type is private;
    package Ada.Storage_IO is
       pragma Preelaborate(Storage_IO);

4      Buffer_Size : constant System.Storage_Elements.Storage_Count := implemen\
tation-defined;
       subtype Buffer_Type is System.Storage_Elements.Storage_Array(1..Buffer_S\
ize);

5      -- Input and output operations

6      procedure Read (Buffer : in  Buffer_Type; Item : out Element_Type);

7      procedure Write(Buffer : out Buffer_Type; Item : in  Element_Type);

8      -- Exceptions

9      Data_Error   : exception renames IO_Exceptions.Data_Error;
    end Ada.Storage_IO;

10   In each instance, the constant Buffer_Size has a value that is the size
(in storage elements) of the buffer required to represent the content of an
object of subtype Element_Type, including any implicit levels of indirection
used by the implementation.

        10.a   Reason:  As with Direct_IO, the Element_Type formal of
        Storage_IO does not have an unknown_discriminant_part so that there
        is a well-defined upper bound on the size of the buffer needed to
        hold the content of an object of the formal subtype (i.e. Buffer_
        Size).  If there are no implicit levels of indirection, Buffer_Size
        will typically equal:

10.b        (Element_Type'Size + System.Storage_Unit - 1) / System.Storage_Unit

        10.c   Implementation defined:  The value of Buffer_Size in
        Storage_IO.

The Read and Write procedures of Storage_IO correspond to the Read and Write
procedures of Direct_IO (see A.8.4), but with the content of the Item
parameter being read from or written into the specified Buffer, rather than
an external file.


     NOTES
11   (21) A buffer used for Storage_IO holds only one element at a time; an
     external file used for Direct_IO holds a sequence of elements.



A.10 Text Input-Output

                              Static Semantics

1   This clause describes the package Text_IO, which provides facilities for
input and output in human-readable form.  Each file is read or written
sequentially, as a sequence of characters grouped into lines, and as a
sequence of lines grouped into pages.  The specification of the package is
given below in subclause A.10.1.

2   The facilities for file management given above, in subclauses A.8.2 and
A.8.3, are available for text input-output.  In place of Read and Write,
however, there are procedures Get and Put that input values of suitable types
from text files, and output values to them.  These values are provided to the
Put procedures, and returned by the Get procedures, in a parameter Item.
Several overloaded procedures of these names exist, for different types of
Item.  These Get procedures analyze the input sequences of characters based
on lexical elements (see Section 2) and return the corresponding values; the
Put procedures output the given values as appropriate lexical elements.
Procedures Get and Put are also available that input and output individual
characters treated as character values rather than as lexical elements.
Related to character input are procedures to look ahead at the next character
without reading it, and to read a character ``immediately'' without waiting
for an end-of-line to signal availability.

3   In addition to the procedures Get and Put for numeric and enumeration
types of Item that operate on text files, analogous procedures are provided
that read from and write to a parameter of type String.  These procedures
perform the same analysis and composition of character sequences as their
counterparts which have a file parameter.

4   For all Get and Put procedures that operate on text files, and for many
other subprograms, there are forms with and without a file parameter.  Each
such Get procedure operates on an input file, and each such Put procedure
operates on an output file.  If no file is specified, a default input file or
a default output file is used.

5   {standard input file} {standard output file} At the beginning of program
execution the default input and output files are the so-called standard input
file and standard output file.  These files are open, have respectively the
current modes In_File and Out_File, and are associated with two
implementation-defined external files.  Procedures are provided to change the
current default input file and the current default output file.

        5.a   Implementation defined:  external files for standard input,
        standard output, and standard error

6   {standard error file} At the beginning of program execution a default
file for program-dependent error-related text output is the so-called
standard error file.  This file is open, has the current mode Out_File, and
is associated with an implementation-defined external file.  A procedure is
provided to change the current default error file.

7   {line terminator} {page terminator} {file terminator} From a logical
point of view, a text file is a sequence of pages, a page is a sequence of
lines, and a line is a sequence of characters; the end of a line is marked by
a line terminator; the end of a page is marked by the combination of a line
terminator immediately followed by a page terminator; and the end of a file
is marked by the combination of a line terminator immediately followed by a
page terminator and then a file terminator.  Terminators are generated during
output; either by calls of procedures provided expressly for that purpose; or
implicitly as part of other operations, for example, when a bounded line
length, a bounded page length, or both, have been specified for a file.

8   The actual nature of terminators is not defined by the language and hence
depends on the implementation.  Although terminators are recognized or
generated by certain of the procedures that follow, they are not necessarily
implemented as characters or as sequences of characters.  Whether they are
characters (and if so which ones) in any particular implementation need not
concern a user who neither explicitly outputs nor explicitly inputs control
characters.  The effect of input (Get) or output (Put) of control characters
(other than horizontal tabulation) is not specified by the language.
{unspecified [partial]}

9   {column number} {current column number} {current line number} {current
page number} The characters of a line are numbered, starting from one; the
number of a character is called its column number.  For a line terminator, a
column number is also defined: it is one more than the number of characters
in the line.  The lines of a page, and the pages of a file, are similarly
numbered.  The current column number is the column number of the next
character or line terminator to be transferred.  The current line number is
the number of the current line.  The current page number is the number of the
current page.  These numbers are values of the subtype Positive_Count of the
type Count (by convention, the value zero of the type Count is used to
indicate special conditions).

10  type Count is range 0 .. implementation-defined;
    subtype Positive_Count is Count range 1 .. Count'Last;

11   {maximum line length} {maximum page length} For an output file or an
append file, a maximum line length can be specified and a maximum page length
can be specified.  If a value to be output cannot fit on the current line,
for a specified maximum line length, then a new line is automatically started
before the value is output; if, further, this new line cannot fit on the
current page, for a specified maximum page length, then a new page is
automatically started before the value is output.  Functions are provided to
determine the maximum line length and the maximum page length.  When a file
is opened with mode Out_File or Append_File, both values are zero: by
convention, this means that the line lengths and page lengths are unbounded.
(Consequently, output consists of a single line if the subprograms for
explicit control of line and page structure are not used.)  The constant
Unbounded is provided for this purpose.


                            Extensions to Ada 83

        11.a   {extensions to Ada 83} Append_File is new in Ada 9X.



A.10.1 The Package Text_IO

                              Static Semantics

1   The library package Text_IO has the following declaration:

2   with Ada.IO_Exceptions;
    package Ada.Text_IO is

3      type File_Type is limited private;

4      type File_Mode is (In_File, Out_File, Append_File);

5      type Count is range 0 .. implementation-defined;
       subtype Positive_Count is Count range 1 .. Count'Last;
       Unbounded : constant Count := 0; -- line and page length

6      subtype Field       is Integer range 0 .. implementation-defined;
       subtype Number_Base is Integer range 2 .. 16;

7      type Type_Set is (Lower_Case, Upper_Case);

8      -- File Management
9      procedure Create (File : in out File_Type;
                         Mode : in File_Mode := Out_File;
                         Name : in String    := "";
                         Form : in String    := "");

10     procedure Open   (File : in out File_Type;
                         Mode : in File_Mode;
                         Name : in String;
                         Form : in String := "");

11     procedure Close  (File : in out File_Type);
       procedure Delete (File : in out File_Type);
       procedure Reset  (File : in out File_Type; Mode : in File_Mode);
       procedure Reset  (File : in out File_Type);

12     function  Mode   (File : in File_Type) return File_Mode;
       function  Name   (File : in File_Type) return String;
       function  Form   (File : in File_Type) return String;

13     function  Is_Open(File : in File_Type) return Boolean;

14     -- Control of default input and output files

15     procedure Set_Input (File : in File_Type);
       procedure Set_Output(File : in File_Type);
       procedure Set_Error (File : in File_Type);

16     function Standard_Input  return File_Type;
       function Standard_Output return File_Type;
       function Standard_Error  return File_Type;

17     function Current_Input   return File_Type;
       function Current_Output  return File_Type;
       function Current_Error   return File_Type;

18     type File_Access is access constant File_Type;

19     function Standard_Input  return File_Access;{94-4527.a}
       function Standard_Output return File_Access;
       function Standard_Error  return File_Access;

20     function Current_Input   return File_Access;
       function Current_Output  return File_Access;
       function Current_Error   return File_Access;

21  --Buffer control
       procedure Flush (File : in out File_Type);
       procedure Flush;

22     -- Specification of line and page lengths

23     procedure Set_Line_Length(File : in File_Type; To : in Count);
       procedure Set_Line_Length(To   : in Count);

24     procedure Set_Page_Length(File : in File_Type; To : in Count);
       procedure Set_Page_Length(To   : in Count);

25     function  Line_Length(File : in File_Type) return Count;
       function  Line_Length return Count;

26     function  Page_Length(File : in File_Type) return Count;
       function  Page_Length return Count;

27     -- Column, Line, and Page Control

28     procedure New_Line   (File    : in File_Type;
                             Spacing : in Positive_Count := 1);
       procedure New_Line   (Spacing : in Positive_Count := 1);

29     procedure Skip_Line  (File    : in File_Type;
                             Spacing : in Positive_Count := 1);
       procedure Skip_Line  (Spacing : in Positive_Count := 1);

30     function  End_Of_Line(File : in File_Type) return Boolean;
       function  End_Of_Line return Boolean;

31     procedure New_Page   (File : in File_Type);
       procedure New_Page;

32     procedure Skip_Page  (File : in File_Type);
       procedure Skip_Page;

33     function  End_Of_Page(File : in File_Type) return Boolean;
       function  End_Of_Page return Boolean;

34     function  End_Of_File(File : in File_Type) return Boolean;
       function  End_Of_File return Boolean;

35     procedure Set_Col (File : in File_Type; To : in Positive_Count);
       procedure Set_Col (To   : in Positive_Count);

36     procedure Set_Line(File : in File_Type; To : in Positive_Count);
       procedure Set_Line(To   : in Positive_Count);

37     function Col (File : in File_Type) return Positive_Count;
       function Col  return Positive_Count;

38     function Line(File : in File_Type) return Positive_Count;
       function Line return Positive_Count;

39     function Page(File : in File_Type) return Positive_Count;
       function Page return Positive_Count;

40     -- Character Input-Output

41     procedure Get(File : in  File_Type; Item : out Character);
       procedure Get(Item : out Character);

42     procedure Put(File : in  File_Type; Item : in Character);
       procedure Put(Item : in  Character);

43     procedure Look_Ahead (File        : in  File_Type;
                             Item        : out Character;
                             End_Of_Line : out Boolean);
       procedure Look_Ahead (Item        : out Character;
                             End_Of_Line : out Boolean);

44     procedure Get_Immediate(File      : in  File_Type;
                               Item      : out Character);
       procedure Get_Immediate(Item      : out Character);

45     procedure Get_Immediate(File      : in  File_Type;
                               Item      : out Character;
                               Available : out Boolean);
       procedure Get_Immediate(Item      : out Character;
                               Available : out Boolean);

46     -- String Input-Output

47     procedure Get(File : in  File_Type; Item : out String);
       procedure Get(Item : out String);

48     procedure Put(File : in  File_Type; Item : in String);
       procedure Put(Item : in  String);

49     procedure Get_Line(File : in  File_Type;
                          Item : out String;
                          Last : out Natural);
       procedure Get_Line(Item : out String; Last : out Natural);

50     procedure Put_Line(File : in  File_Type; Item : in String);
       procedure Put_Line(Item : in  String);

51  -- Generic packages for Input-Output of Integer Types

52     generic
          type Num is range <>;
       package Integer_IO is

53        Default_Width : Field := Num'Width;
          Default_Base  : Number_Base := 10;

54        procedure Get(File  : in  File_Type;
                        Item  : out Num;
                        Width : in Field := 0);
          procedure Get(Item  : out Num;
                        Width : in  Field := 0);

55        procedure Put(File  : in File_Type;
                        Item  : in Num;
                        Width : in Field := Default_Width;
                        Base  : in Number_Base := Default_Base);
          procedure Put(Item  : in Num;
                        Width : in Field := Default_Width;
                        Base  : in Number_Base := Default_Base);
          procedure Get(From : in  String;
                        Item : out Num;
                        Last : out Positive);
          procedure Put(To   : out String;
                        Item : in Num;
                        Base : in Number_Base := Default_Base);

56     end Integer_IO;

57     generic
          type Num is mod <>;
       package Modular_IO is

58        Default_Width : Field := Num'Width;
          Default_Base  : Number_Base := 10;

59        procedure Get(File  : in  File_Type;
                        Item  : out Num;
                        Width : in Field := 0);
          procedure Get(Item  : out Num;
                        Width : in  Field := 0);

60        procedure Put(File  : in File_Type;
                        Item  : in Num;
                        Width : in Field := Default_Width;
                        Base  : in Number_Base := Default_Base);
          procedure Put(Item  : in Num;
                        Width : in Field := Default_Width;
                        Base  : in Number_Base := Default_Base);
          procedure Get(From : in  String;
                        Item : out Num;
                        Last : out Positive);
          procedure Put(To   : out String;
                        Item : in Num;
                        Base : in Number_Base := Default_Base);
61     end Modular_IO;

62     -- Generic packages for Input-Output of Real Types

63     generic
          type Num is digits <>;
       package Float_IO is

64        Default_Fore : Field := 2;
          Default_Aft  : Field := Num'Digits-1;
          Default_Exp  : Field := 3;

65        procedure Get(File  : in  File_Type;
                        Item  : out Num;
                        Width : in  Field := 0);
          procedure Get(Item  : out Num;
                        Width : in  Field := 0);

66        procedure Put(File : in File_Type;
                        Item : in Num;
                        Fore : in Field := Default_Fore;
                        Aft  : in Field := Default_Aft;
                        Exp  : in Field := Default_Exp);
          procedure Put(Item : in Num;
                        Fore : in Field := Default_Fore;
                        Aft  : in Field := Default_Aft;
                        Exp  : in Field := Default_Exp);

67        procedure Get(From : in String;
                        Item : out Num;
                        Last : out Positive);
          procedure Put(To   : out String;
                        Item : in Num;
                        Aft  : in Field := Default_Aft;
                        Exp  : in Field := Default_Exp);
       end Float_IO;

68     generic
          type Num is delta <>;
       package Fixed_IO is

69        Default_Fore : Field := Num'Fore;
          Default_Aft  : Field := Num'Aft;
          Default_Exp  : Field := 0;

70        procedure Get(File  : in  File_Type;
                        Item  : out Num;
                        Width : in  Field := 0);
          procedure Get(Item  : out Num;
                        Width : in  Field := 0);

71        procedure Put(File : in File_Type;
                        Item : in Num;
                        Fore : in Field := Default_Fore;
                        Aft  : in Field := Default_Aft;
                        Exp  : in Field := Default_Exp);
          procedure Put(Item : in Num;
                        Fore : in Field := Default_Fore;
                        Aft  : in Field := Default_Aft;
                        Exp  : in Field := Default_Exp);

72        procedure Get(From : in  String;
                        Item : out Num;
                        Last : out Positive);
          procedure Put(To   : out String;
                        Item : in Num;
                        Aft  : in Field := Default_Aft;
                        Exp  : in Field := Default_Exp);
       end Fixed_IO;

73     generic
          type Num is delta <> digits <>;
       package Decimal_IO is

74        Default_Fore : Field := Num'Fore;
          Default_Aft  : Field := Num'Aft;
          Default_Exp  : Field := 0;

75        procedure Get(File  : in  File_Type;
                        Item  : out Num;
                        Width : in  Field := 0);
          procedure Get(Item  : out Num;
                        Width : in  Field := 0);

76        procedure Put(File : in File_Type;
                        Item : in Num;
                        Fore : in Field := Default_Fore;
                        Aft  : in Field := Default_Aft;
                        Exp  : in Field := Default_Exp);
          procedure Put(Item : in Num;
                        Fore : in Field := Default_Fore;
                        Aft  : in Field := Default_Aft;
                        Exp  : in Field := Default_Exp);

77        procedure Get(From : in  String;
                        Item : out Num;
                        Last : out Positive);
          procedure Put(To   : out String;
                        Item : in Num;
                        Aft  : in Field := Default_Aft;
                        Exp  : in Field := Default_Exp);
       end Decimal_IO;

78     -- Generic package for Input-Output of Enumeration Types

79     generic
          type Enum is (<>);
       package Enumeration_IO is

80        Default_Width   : Field := 0;
          Default_Setting : Type_Set := Upper_Case;

81        procedure Get(File : in  File_Type;
                        Item : out Enum);
          procedure Get(Item : out Enum);

82        procedure Put(File  : in File_Type;
                        Item  : in Enum;
                        Width : in Field    := Default_Width;
                        Set   : in Type_Set := Default_Setting);
          procedure Put(Item  : in Enum;
                        Width : in Field    := Default_Width;
                        Set   : in Type_Set := Default_Setting);

83        procedure Get(From : in  String;
                        Item : out Enum;
                        Last : out Positive);
          procedure Put(To   : out String;
                        Item : in  Enum;
                        Set  : in  Type_Set := Default_Setting);
       end Enumeration_IO;

84  -- Exceptions

85     Status_Error : exception renames IO_Exceptions.Status_Error;
       Mode_Error   : exception renames IO_Exceptions.Mode_Error;
       Name_Error   : exception renames IO_Exceptions.Name_Error;
       Use_Error    : exception renames IO_Exceptions.Use_Error;
       Device_Error : exception renames IO_Exceptions.Device_Error;
       End_Error    : exception renames IO_Exceptions.End_Error;
       Data_Error   : exception renames IO_Exceptions.Data_Error;
       Layout_Error : exception renames IO_Exceptions.Layout_Error;
    private
       ... -- not specified by the language
    end Ada.Text_IO;


                        Incompatibilities With Ada 83

        85.a   {incompatibilities with Ada 83} Append_File is a new element
        of enumeration type File_Mode.

                            Extensions to Ada 83

        85.b   {extensions to Ada 83} Get_Immediate, Look_Ahead, the
        subprograms for dealing with standard error, the type File_Access and
        its associated subprograms, and the generic packages Modular_IO and
        Decimal_IO are new in Ada 9X.



A.10.2 Text File Management

                              Static Semantics

1   The only allowed file modes for text files are the modes In_File, Out_
File, and Append_File.  The subprograms given in subclause A.8.2 for the
control of external files, and the function End_Of_File given in subclause
A.8.3 for sequential input-output, are also available for text files.  There
is also a version of End_Of_File that refers to the current default input
file.  For text files, the procedures have the following additional effects:

    2  For the procedures Create and Open: After a file with mode Out_
       File or Append_File is opened, the page length and line length
       are unbounded (both have the conventional value zero).  After a
       file (of any mode) is opened, the current column, current line,
       and current page numbers are set to one.  If the mode is Append_
       File, it is implementation defined whether a page terminator will
       separate preexisting text in the file from the new text to be
       written.

 2.a    Reason:  For a file with mode Append_File, although it may seem
        more sensible for Open to set the current column, line, and page
        number based on the number of pages in the file, the number of
        lines on the last page, and the number of columns in the last
        line, we rejected this approach because of implementation costs;
        it would require the implementation to scan the file before
        doing the append, or to do processing that would be equivalent
        in effect.

 2.b    For similar reasons, there is no requirement to erase the last
        page terminator of the file, nor to insert an explicit page
        terminator in the case when the final page terminator of a file
        is represented implicitly by the implementation.

    3  For the procedure Close: If the file has the current mode Out_
       File or Append_File, has the effect of calling New_Page, unless
       the current page is already terminated; then outputs a file
       terminator.

    4  For the procedure Reset: If the file has the current mode Out_
       File or Append_File, has the effect of calling New_Page, unless
       the current page is already terminated; then outputs a file
       terminator.  The current column, line, and page numbers are set
       to one, and the line and page lengths to Unbounded.  If the new
       mode is Append_File, it is implementation defined whether a page
       terminator will separate preexisting text in the file from the
       new text to be written.

 4.a    Reason:  The behavior of Reset should be similar to closing a
        file and reopening it with the given mode

5   The exception Mode_Error is propagated by the procedure Reset upon an
attempt to change the mode of a file that is the current default input file,
the current default output file, or the current default error file.


     NOTES
6    (22) An implementation can define the Form parameter of Create and Open
     to control effects including the following:

         7  the interpretation of line and column numbers for an
            interactive file, and

         8  the interpretation of text formats in a file created by a
            foreign program.



A.10.3 Default Input, Output, and Error Files

                              Static Semantics

1   The following subprograms provide for the control of the particular
default files that are used when a file parameter is omitted from a Get, Put,
or other operation of text input-output described below, or when
application-dependent error-related text is to be output.


2   procedure Set_Input(File : in File_Type);

        3   Operates on a file of mode In_File.  Sets the current default
        input file to File.
        4   The exception Status_Error is propagated if the given file is not
        open.  The exception Mode_Error is propagated if the mode of the
        given file is not In_File.  {94-4527.a} {94-4972.a}


5   procedure Set_Output(File : in File_Type);
    procedure Set_Error (File : in File_Type);

        6   Each operates on a file of mode Out_File or Append_File.  Set_
        Output sets the current default output file to File.  Set_Error sets
        the current default error file to File.  The exception Status_Error
        is propagated if the given file is not open.  The exception Mode_
        Error is propagated if the mode of the given file is not Out_File or
        Append_File.  {94-4527.a} {94-4972.a}


7   function Standard_Input return File_Type;
    function Standard_Input return File_Access;

        8   Returns the standard input file (see A.10), or an access value
        designating the standard input file, respectively.


9   function Standard_Output return File_Type;
    function Standard_Output return File_Access;

        10   Returns the standard output file (see A.10) or an access value
        designating the standard output file, respectively.


11  function Standard_Error return File_Type;
    function Standard_Error return File_Access;

        12   Returns the standard error file (see A.10), or an access value
        designating the standard output file, respectively.
        13   The Form strings implicitly associated with the opening of
        Standard_Input, Standard_Output, and Standard_Error at the start of
        program execution are implementation defined.


14  function Current_Input return File_Type;
    function Current_Input return File_Access;

        15   Returns the current default input file, or an access value
        designating the current default input file, respectively.


16  function Current_Output return File_Type;
    function Current_Output return File_Access;

        17   Returns the current default output file, or an access value
        designating the current default output file, respectively.


18  function Current_Error return File_Type;
    function Current_Error return File_Access;

        19   Returns the current default error file, or an access value
        designating the current default error file, respectively.
        {94-4975.a}


20  procedure Flush (File : in out File_Type);
    procedure Flush;

        21   The effect of Flush is the same as the corresponding subprogram
        in Streams.Stream_IO (see A.12.1).  If File is not explicitly
        specified, Current_Output is used.


                             Erroneous Execution

22   {erroneous execution} The execution of a program is erroneous if it
attempts to use a current default input, default output, or default error
file that no longer exists.

23   If the Close operation is applied to a file object that is also serving
as the default input, default output, or default error file, then subsequent
operations on such a default file are erroneous.


     NOTES
24   (23) The standard input, standard output, and standard error files
     cannot be opened, closed, reset, or deleted, because the parameter File
     of the corresponding procedures has the mode in out.

25   (24) The standard input, standard output, and standard error files are
     different file objects, but not necessarily different external files.



A.10.4 Specification of Line and Page Lengths

                              Static Semantics

1   The subprograms described in this subclause are concerned with the line
and page structure of a file of mode Out_File or Append_File.  They operate
either on the file given as the first parameter, or, in the absence of such a
file parameter, on the current default output file.  They provide for output
of text with a specified maximum line length or page length.  In these cases,
line and page terminators are output implicitly and automatically when
needed.  When line and page lengths are unbounded (that is, when they have
the conventional value zero), as in the case of a newly opened file, new
lines and new pages are only started when explicitly called for.

2   In all cases, the exception Status_Error is propagated if the file to be
used is not open; the exception Mode_Error is propagated if the mode of the
file is not Out_File or Append_File.


3   procedure Set_Line_Length(File : in File_Type; To : in Count);
    procedure Set_Line_Length(To   : in Count);

        4   Sets the maximum line length of the specified output or append
        file to the number of characters specified by To.  The value zero for
        To specifies an unbounded line length.

        4.a   Ramification:  The setting does not affect the lengths of lines
        in the existing file, rather it only influences subsequent output
        operations.

        5   The exception Use_Error is propagated if the specified line
        length is inappropriate for the associated external file.


6   procedure Set_Page_Length(File : in File_Type; To : in Count);
    procedure Set_Page_Length(To   : in Count);

        7   Sets the maximum page length of the specified output or append
        file to the number of lines specified by To.  The value zero for To
        specifies an unbounded page length.
        8   The exception Use_Error is propagated if the specified page
        length is inappropriate for the associated external file.


9   function Line_Length(File : in File_Type) return Count;
    function Line_Length return Count;

        10   Returns the maximum line length currently set for the specified
        output or append file, or zero if the line length is unbounded.


11  function Page_Length(File : in File_Type) return Count;
    function Page_Length return Count;

        12   Returns the maximum page length currently set for the specified
        output or append file, or zero if the page length is unbounded.



A.10.5 Operations on Columns, Lines, and Pages

                              Static Semantics

1   The subprograms described in this subclause provide for explicit control
of line and page structure; they operate either on the file given as the
first parameter, or, in the absence of such a file parameter, on the
appropriate (input or output) current default file.  The exception Status_
Error is propagated by any of these subprograms if the file to be used is not
open.


2   procedure New_Line(File : in File_Type; Spacing : in Positive_Count := 1);
    procedure New_Line(Spacing : in Positive_Count := 1);

        3   Operates on a file of mode Out_File or Append_File.
        4   For a Spacing of one: Outputs a line terminator and sets the
        current column number to one.  Then increments the current line
        number by one, except in the case that the current line number is
        already greater than or equal to the maximum page length, for a
        bounded page length; in that case a page terminator is output, the
        current page number is incremented by one, and the current line
        number is set to one.
        5   For a Spacing greater than one, the above actions are performed
        Spacing times.
        6   The exception Mode_Error is propagated if the mode is not Out_
        File or Append_File.


7   procedure Skip_Line(File  : in File_Type; Spacing : in Positive_Count := 1);
    procedure Skip_Line(Spacing : in Positive_Count := 1);

        8   Operates on a file of mode In_File.
        9   For a Spacing of one: Reads and discards all characters until a
        line terminator has been read, and then sets the current column
        number to one.  If the line terminator is not immediately followed by
        a page terminator, the current line number is incremented by one.
        Otherwise, if the line terminator is immediately followed by a page
        terminator, then the page terminator is skipped, the current page
        number is incremented by one, and the current line number is set to
        one.
        10   For a Spacing greater than one, the above actions are performed
        Spacing times.
        11   The exception Mode_Error is propagated if the mode is not In_
        File.  The exception End_Error is propagated if an attempt is made to
        read a file terminator.


12  function End_Of_Line(File : in File_Type) return Boolean;
    function End_Of_Line return Boolean;

        13   Operates on a file of mode In_File.  Returns True if a line
        terminator or a file terminator is next; otherwise returns False.
        14   The exception Mode_Error is propagated if the mode is not In_
        File.


15  procedure New_Page(File : in File_Type);
    procedure New_Page;

        16   Operates on a file of mode Out_File or Append_File.  Outputs a
        line terminator if the current line is not terminated, or if the
        current page is empty (that is, if the current column and line
        numbers are both equal to one).  Then outputs a page terminator,
        which terminates the current page.  Adds one to the current page
        number and sets the current column and line numbers to one.
        17   The exception Mode_Error is propagated if the mode is not Out_
        File or Append_File.


18  procedure Skip_Page(File : in File_Type);
    procedure Skip_Page;

        19   Operates on a file of mode In_File.  Reads and discards all
        characters and line terminators until a page terminator has been
        read.  Then adds one to the current page number, and sets the current
        column and line numbers to one.
        20   The exception Mode_Error is propagated if the mode is not In_
        File.  The exception End_Error is propagated if an attempt is made to
        read a file terminator.


21  function End_Of_Page(File : in File_Type) return Boolean;
    function End_Of_Page return Boolean;

        22   Operates on a file of mode In_File.  Returns True if the
        combination of a line terminator and a page terminator is next, or if
        a file terminator is next; otherwise returns False.
        23   The exception Mode_Error is propagated if the mode is not In_
        File.


24  function End_Of_File(File : in File_Type) return Boolean;
    function End_Of_File return Boolean;

        25   Operates on a file of mode In_File.  Returns True if a file
        terminator is next, or if the combination of a line, a page, and a
        file terminator is next; otherwise returns False.
        26   The exception Mode_Error is propagated if the mode is not In_
        File.
        27   The following subprograms provide for the control of the current
        position of reading or writing in a file.  In all cases, the default
        file is the current output file.


28  procedure Set_Col(File : in File_Type; To : in Positive_Count);
    procedure Set_Col(To   : in Positive_Count);

        29   If the file mode is Out_File or Append_File:

           30  If the value specified by To is greater than the current
               column number, outputs spaces, adding one to the current
               column number after each space, until the current column
               number equals the specified value.  If the value
               specified by To is equal to the current column number,
               there is no effect.  If the value specified by To is less
               than the current column number, has the effect of calling
               New_Line (with a spacing of one), then outputs (To - 1)
               spaces, and sets the current column number to the
               specified value.

           31  The exception Layout_Error is propagated if the value
               specified by To exceeds Line_Length when the line length
               is bounded (that is, when it does not have the
               conventional value zero).

        32   If the file mode is In_File:

           33  Reads (and discards) individual characters, line
               terminators, and page terminators, until the next
               character to be read has a column number that equals the
               value specified by To; there is no effect if the current
               column number already equals this value.  Each transfer
               of a character or terminator maintains the current
               column, line, and page numbers in the same way as a Get
               procedure (see A.10.6).  (Short lines will be skipped
               until a line is reached that has a character at the
               specified column position.)

           34  The exception End_Error is propagated if an attempt is
               made to read a file terminator.


35  procedure Set_Line(File : in File_Type; To : in Positive_Count);
    procedure Set_Line(To   : in Positive_Count);

        36   If the file mode is Out_File or Append_File:

           37  If the value specified by To is greater than the current
               line number, has the effect of repeatedly calling New_
               Line (with a spacing of one), until the current line
               number equals the specified value.  If the value
               specified by To is equal to the current line number,
               there is no effect.  If the value specified by To is less
               than the current line number, has the effect of calling
               New_Page followed by a call of New_Line with a spacing
               equal to (To - 1).

           38  The exception Layout_Error is propagated if the value
               specified by To exceeds Page_Length when the page length
               is bounded (that is, when it does not have the
               conventional value zero).

        39   If the mode is In_File:

           40  Has the effect of repeatedly calling Skip_Line (with a
               spacing of one), until the current line number equals the
               value specified by To; there is no effect if the current
               line number already equals this value.  (Short pages will
               be skipped until a page is reached that has a line at the
               specified line position.)

           41  The exception End_Error is propagated if an attempt is
               made to read a file terminator.


42  function Col(File : in File_Type) return Positive_Count;
    function Col return Positive_Count;

        43   Returns the current column number.
        44   The exception Layout_Error is propagated if this number exceeds
        Count'Last.


45  function Line(File : in File_Type) return Positive_Count;
    function Line return Positive_Count;

        46   Returns the current line number.
        47   The exception Layout_Error is propagated if this number exceeds
        Count'Last.


48  function Page(File : in File_Type) return Positive_Count;
    function Page return Positive_Count;

        49   Returns the current page number.
        50   The exception Layout_Error is propagated if this number exceeds
        Count'Last.

51   The column number, line number, or page number are allowed to exceed
Count'Last (as a consequence of the input or output of sufficiently many
characters, lines, or pages).  These events do not cause any exception to be
propagated.  However, a call of Col, Line, or Page propagates the exception
Layout_Error if the corresponding number exceeds Count'Last.
     NOTES
52   (25) A page terminator is always skipped whenever the preceding line
     terminator is skipped.  An implementation may represent the combination
     of these terminators by a single character, provided that it is properly
     recognized on input.



A.10.6 Get and Put Procedures

                              Static Semantics

1   The procedures Get and Put for items of the type Character, String,
numeric types, and enumeration types are described in subsequent subclauses.
Features of these procedures that are common to most of these types are
described in this subclause.  The Get and Put procedures for items of type
Character and String deal with individual character values; the Get and Put
procedures for numeric and enumeration types treat the items as lexical
elements.

2   All procedures Get and Put have forms with a file parameter, written
first.  Where this parameter is omitted, the appropriate (input or output)
current default file is understood to be specified.  Each procedure Get
operates on a file of mode In_File.  Each procedure Put operates on a file of
mode Out_File or Append_File.

3   All procedures Get and Put maintain the current column, line, and page
numbers of the specified file: the effect of each of these procedures upon
these numbers is the result of the effects of individual transfers of
characters and of individual output or skipping of terminators.  Each
transfer of a character adds one to the current column number.  Each output
of a line terminator sets the current column number to one and adds one to
the current line number.  Each output of a page terminator sets the current
column and line numbers to one and adds one to the current page number.  For
input, each skipping of a line terminator sets the current column number to
one and adds one to the current line number; each skipping of a page
terminator sets the current column and line numbers to one and adds one to
the current page number.  Similar considerations apply to the procedures Get_
Line, Put_Line, and Set_Col.

4   Several Get and Put procedures, for numeric and enumeration types, have
format parameters which specify field lengths; these parameters are of the
nonnegative subtype Field of the type Integer.

5   {blank (in text input for enumeration and numeric types)} Input-output of
enumeration values uses the syntax of the corresponding lexical elements.
Any Get procedure for an enumeration type begins by skipping any leading
blanks, or line or page terminators.  Get procedures for numeric or
enumeration types start by skipping leading blanks, where a blank is defined
as a space or a horizontal tabulation character.  Next, characters are input
only so long as the sequence input is an initial sequence of an identifier or
of a character literal (in particular, input ceases when a line terminator is
encountered).  The character or line terminator that causes input to cease
remains available for subsequent input.

6   For a numeric type, the Get procedures have a format parameter called
Width.  If the value given for this parameter is zero, the Get procedure
proceeds in the same manner as for enumeration types, but using the syntax of
numeric literals instead of that of enumeration literals.  If a nonzero value
is given, then exactly Width characters are input, or the characters up to a
line terminator, whichever comes first; any skipped leading blanks are
included in the count.  The syntax used for numeric literals is an extended
syntax that allows a leading sign (but no intervening blanks, or line or page
terminators) and that also allows (for real types) an integer literal as well
as forms that have digits only before the point or only after the point.

7   Any Put procedure, for an item of a numeric or an enumeration type,
outputs the value of the item as a numeric literal, identifier, or character
literal, as appropriate.  This is preceded by leading spaces if required by
the format parameters Width or Fore (as described in later subclauses), and
then a minus sign for a negative value; for an enumeration type, the spaces
follow instead of leading.  The format given for a Put procedure is
overridden if it is insufficiently wide, by using the minimum needed width.

8   Two further cases arise for Put procedures for numeric and enumeration
types, if the line length of the specified output file is bounded (that is,
if it does not have the conventional value zero).  If the number of
characters to be output does not exceed the maximum line length, but is such
that they cannot fit on the current line, starting from the current column,
then (in effect) New_Line is called (with a spacing of one) before output of
the item.  Otherwise, if the number of characters exceeds the maximum line
length, then the exception Layout_Error is propagated and nothing is output.

9   The exception Status_Error is propagated by any of the procedures Get,
Get_Line, Put, and Put_Line if the file to be used is not open.  The
exception Mode_Error is propagated by the procedures Get and Get_Line if the
mode of the file to be used is not In_File; and by the procedures Put and
Put_Line, if the mode is not Out_File or Append_File.

10   The exception End_Error is propagated by a Get procedure if an attempt
is made to skip a file terminator.  The exception Data_Error is propagated by
a Get procedure if the sequence finally input is not a lexical element
corresponding to the type, in particular if no characters were input; for
this test, leading blanks are ignored; for an item of a numeric type, when a
sign is input, this rule applies to the succeeding numeric literal.  The
exception Layout_Error is propagated by a Put procedure that outputs to a
parameter of type String, if the length of the actual string is insufficient
for the output of the item.


                                  Examples

11   In the examples, here and in subclauses A.10.8 and A.10.9, the string
quotes and the lower case letter b are not transferred: they are shown only
to reveal the layout and spaces.

12  N : Integer;
       ...
    Get(N);

13
    --      Characters at input       Sequence input            Value of N

    --      bb-12535b                 -12535                    -12535
    --      bb12_535e1b               12_535e1                  125350
    --      bb12_535e;                12_535e                   (none) Data_Err\
or raised

14   Example of overridden width parameter:

15  Put(Item => -23, Width => 2);  --  "-23"



A.10.7 Input-Output of Characters and Strings

                              Static Semantics

1   For an item of type Character the following procedures are provided:


2   procedure Get(File : in File_Type; Item : out Character);
    procedure Get(Item : out Character);

        3   After skipping any line terminators and any page terminators,
        reads the next character from the specified input file and returns
        the value of this character in the out parameter Item.
        4   The exception End_Error is propagated if an attempt is made to
        skip a file terminator.


5   procedure Put(File : in File_Type; Item : in Character);
    procedure Put(Item : in Character);

        6   If the line length of the specified output file is bounded (that
        is, does not have the conventional value zero), and the current
        column number exceeds it, has the effect of calling New_Line with a
        spacing of one.  Then, or otherwise, outputs the given character to
        the file.


7   procedure Look_Ahead (File        : in  File_Type;
                          Item        : out Character;
                          End_Of_Line : out Boolean);
    procedure Look_Ahead (Item        : out Character;
                          End_Of_Line : out Boolean);

        8   Mode_Error is propagated if the mode of the file is not In_File.
        Sets End_Of_Line to True if at end of line, including if at end of
        page or at end of file; in each of these cases the value of Item is
        not specified.  {unspecified [partial]} Otherwise End_Of_Line is set
        to False and Item is set to the the next character (without consuming
        it) from the file.


9   procedure Get_Immediate(File : in  File_Type;
                            Item : out Character);
    procedure Get_Immediate(Item : out Character);

        10   Reads the next character, either control or graphic, from the
        specified File or the default input file.  Mode_Error is propagated
        if the mode of the file is not In_File.  End_Error is propagated if
        at the end of the file.  The current column, line and page numbers
        for the file are not affected.


11  procedure Get_Immediate(File      : in  File_Type;
                            Item      : out Character;
                            Available : out Boolean);
    procedure Get_Immediate(Item      : out Character;
                            Available : out Boolean);

        12   If a character, either control or graphic, is available from the
        specified File or the default input file, then the character is read;
        Available is True and Item contains the value of this character.  If
        a character is not available, then Available is False and the value
        of Item is not specified.  {unspecified [partial]} Mode_Error is
        propagated if the mode of the file is not In_File.  End_Error is
        propagated if at the end of the file.  The current column, line and
        page numbers for the file are not affected.
        13   For an item of type String the following procedures are
        provided:


14  procedure Get(File : in File_Type; Item : out String);
    procedure Get(Item : out String);

        15   Determines the length of the given string and attempts that
        number of Get operations for successive characters of the string (in
        particular, no operation is performed if the string is null).
16  procedure Put(File : in File_Type; Item : in String);
    procedure Put(Item : in String);

        17   Determines the length of the given string and attempts that
        number of Put operations for successive characters of the string (in
        particular, no operation is performed if the string is null).


18  procedure Get_Line(File : in File_Type; Item : out String; Last : out Natur\
al);
    procedure Get_Line(Item : out String;   Last : out Natural);

        19   Reads successive characters from the specified input file and
        assigns them to successive characters of the specified string.
        Reading stops if the end of the string is met.  Reading also stops if
        the end of the line is met before meeting the end of the string; in
        this case Skip_Line is (in effect) called with a spacing of 1.
        {unspecified [partial]} The values of characters not assigned are not
        specified.
        20   If characters are read, returns in Last the index value such
        that Item(Last) is the last character assigned (the index of the
        first character assigned is Item'First).  If no characters are read,
        returns in Last an index value that is one less than Item'First.  The
        exception End_Error is propagated if an attempt is made to skip a
        file terminator.


21  procedure Put_Line(File : in File_Type; Item : in String);
    procedure Put_Line(Item : in String);

        22   Calls the procedure Put for the given string, and then the
        procedure New_Line with a spacing of one.


                            Implementation Advice

23   The Get_Immediate procedures should be implemented with unbuffered
input.  For a device such as a keyboard, input should be ``available'' if a
key has already been typed, whereas for a disk file, input should always be
available except at end of file.  For a file associated with a keyboard-like
device, any line-editing features of the underlying operating system should
be disabled during the execution of Get_Immediate.


     NOTES
24   (26) Get_Immediate can be used to read a single key from the keyboard
     ``immediately''; that is, without waiting for an end of line.  In a call
     of Get_Immediate without the parameter Available, the caller will wait
     until a character is available.

25   (27) In a literal string parameter of Put, the enclosing string bracket
     characters are not output.  Each doubled string bracket character in the
     enclosed string is output as a single string bracket character, as a
     consequence of the rule for string literals (see 2.6).

26   (28) A string read by Get or written by Put can extend over several
     lines.  An implementation is allowed to assume that certain external
     files do not contain page terminators, in which case Get_Line and Skip_
     Line can return as soon as a line terminator is read.



A.10.8 Input-Output for Integer Types

                              Static Semantics

1   The following procedures are defined in the generic packages Integer_IO
and Modular_IO, which have to be instantiated for the appropriate signed
integer or modular type respectively (indicated by Num in the
specifications).

2   Values are output as decimal or based literals, without low line
characters or exponent, and, for Integer_IO, preceded by a minus sign if
negative.  The format (which includes any leading spaces and minus sign) can
be specified by an optional field width parameter.  Values of widths of
fields in output formats are of the nonnegative integer subtype Field.
Values of bases are of the integer subtype Number_Base.

3   subtype Number_Base is Integer range 2 .. 16;

4   The default field width and base to be used by output procedures are
defined by the following variables that are declared in the generic packages
Integer_IO and Modular_IO:

5   Default_Width : Field := Num'Width;
    Default_Base  : Number_Base := 10;

6   The following procedures are provided:


7   procedure Get(File : in File_Type; Item : out Num; Width : in Field := 0);
    procedure Get(Item : out Num; Width : in Field := 0);

        8   If the value of the parameter Width is zero, skips any leading
        blanks, line terminators, or page terminators, then reads a plus sign
        if present or (for a signed type only) a minus sign if present, then
        reads the longest possible sequence of characters matching the syntax
        of a numeric literal without a point.  {94-4526.d} If a nonzero value
        of Width is supplied, then exactly Width characters are input, or the
        characters (possibly none) up to a line terminator, whichever comes
        first; any skipped leading blanks are included in the count.
        9   Returns, in the parameter Item, the value of type Num that
        corresponds to the sequence input.
        10   The exception Data_Error is propagated if the sequence of
        characters read does not form a legal integer literal or if the value
        obtained is not of the subtype Num (for Integer_IO) or is not in the
        base range of Num (for Modular_IO).


11  procedure Put(File  : in File_Type;
                  Item  : in Num;
                  Width : in Field := Default_Width;
                  Base  : in Number_Base := Default_Base);

    procedure Put(Item  : in Num;
                  Width : in Field := Default_Width;
                  Base  : in Number_Base := Default_Base);

        12   Outputs the value of the parameter Item as an integer literal,
        with no low lines, no exponent, and no leading zeros (but a single
        zero for the value zero), and a preceding minus sign for a negative
        value.
        13   If the resulting sequence of characters to be output has fewer
        than Width characters, then leading spaces are first output to make
        up the difference.
        14   Uses the syntax for decimal literal if the parameter Base has
        the value ten (either explicitly or through Default_Base); otherwise,
        uses the syntax for based literal, with any letters in upper case.


15  procedure Get(From : in String; Item : out Num; Last : out Positive);

        16   Reads an integer value from the beginning of the given string,
        following the same rules as the Get procedure that reads an integer
        value from a file, but treating the end of the string as a file
        terminator.  Returns, in the parameter Item, the value of type Num
        that corresponds to the sequence input.  Returns in Last the index
        value such that From(Last) is the last character read.
        17   The exception Data_Error is propagated if the sequence input
        does not have the required syntax or if the value obtained is not of
        the subtype Num.


18  procedure Put(To   : out String;
                  Item : in Num;
                  Base : in Number_Base := Default_Base);

        19   Outputs the value of the parameter Item to the given string,
        following the same rule as for output to a file, using the length of
        the given string as the value for Width.

20   Integer_Text_IO is a library package that is a nongeneric equivalent to
Text_IO.Integer_IO for the predefined type Integer:

21  with Ada.Text_IO;
    package Ada.Integer_Text_IO is new Ada.Text_IO.Integer_IO(Integer);

22   For each predefined signed integer type, a nongeneric equivalent to
Text_IO.Integer_IO is provided, with names such as Ada.Long_Integer_Text_IO.

        22.a   Change:  Preinstantiations of Text_IO.Integer_IO added, as per
        WG9 resolution.


                         Implementation Permissions

23   The nongeneric equivalent packages may, but need not, be actual
instantiations of the generic package for the appropriate predefined type.


     NOTES
24   (29) For Modular_IO, execution of Get propagates Data_Error if the
     sequence of characters read forms an integer literal outside the range
     0..Num'Last.


                                  Examples

25

26  package Int_IO is new Integer_IO(Small_Int); use Int_IO;
    -- default format used at instantiation,
    -- Default_Width = 4, Default_Base = 10

27  Put(126);                            -- "b126"
    Put(-126, 7);                        -- "bbb-126"
    Put(126, Width => 13, Base => 2);    -- "bbb2#1111110#"



A.10.9 Input-Output for Real Types

                              Static Semantics

1   The following procedures are defined in the generic packages Float_IO,
Fixed_IO, and Decimal_IO, which have to be instantiated for the appropriate
floating point, ordinary fixed point, or decimal fixed point type
respectively (indicated by Num in the specifications).

2   Values are output as decimal literals without low line characters.  The
format of each value output consists of a Fore field, a decimal point, an Aft
field, and (if a nonzero Exp parameter is supplied) the letter E and an Exp
field.  The two possible formats thus correspond to:

3   Fore  .  Aft

4   and to:

5   Fore  .  Aft  E  Exp

6   without any spaces between these fields.  The Fore field may include
leading spaces, and a minus sign for negative values.  The Aft field includes
only decimal digits (possibly with trailing zeros).  The Exp field includes
the sign (plus or minus) and the exponent (possibly with leading zeros).

7   For floating point types, the default lengths of these fields are defined
by the following variables that are declared in the generic package Float_IO:

8   Default_Fore : Field := 2;
    Default_Aft  : Field := Num'Digits-1;
    Default_Exp  : Field := 3;

9   For ordinary or decimal fixed point types, the default lengths of these
fields are defined by the following variables that are declared in the
generic packages Fixed_IO and Decimal_IO, respectively:

10  Default_Fore : Field := Num'Fore;
    Default_Aft  : Field := Num'Aft;
    Default_Exp  : Field := 0;

11   The following procedures are provided:


12  procedure Get(File : in File_Type; Item : out Num; Width : in Field := 0);
    procedure Get(Item : out Num; Width : in Field := 0);

        13   If the value of the parameter Width is zero, skips any leading
        blanks, line terminators, or page terminators, then reads the longest
        possible sequence of characters matching the syntax of any of the
        following (see 2.4):

           14  [+|-]numeric_literal

           15  [+|-]numeral.[exponent]

           16  [+|-].numeral[exponent]

           17  [+|-]base#based_numeral.#[exponent]

           18  [+|-]base#.based_numeral#[exponent]

        {94-4526.e}
        19   If a nonzero value of Width is supplied, then exactly Width
        characters are input, or the characters (possibly none) up to a line
        terminator, whichever comes first; any skipped leading blanks are
        included in the count.
        20   Returns in the parameter Item the value of type Num that
        corresponds to the sequence input, preserving the sign (positive if
        none has been specified) of a zero value if Num is a floating point
        type and Num'Signed_Zeros is True.  {94-4526.b}
        21   The exception Data_Error is propagated if the sequence input
        does not have the required syntax or if the value obtained is not of
        the subtype Num.


22  procedure Put(File : in File_Type;
                  Item : in Num;
                  Fore : in Field := Default_Fore;
                  Aft  : in Field := Default_Aft;
                  Exp  : in Field := Default_Exp);

    procedure Put(Item : in Num;
                  Fore : in Field := Default_Fore;
                  Aft  : in Field := Default_Aft;
                  Exp  : in Field := Default_Exp);

        23   Outputs the value of the parameter Item as a decimal literal
        with the format defined by Fore, Aft and Exp.  If the value is
        negative, or if Num is a floating point type where Num'Signed_Zeros
        is True and the value is a negatively signed zero, then a minus sign
        is included in the integer part.  {94-4526.b} If Exp has the value
        zero, then the integer part to be output has as many digits as are
        needed to represent the integer part of the value of Item, overriding
        Fore if necessary, or consists of the digit zero if the value of Item
        has no integer part.
        24   If Exp has a value greater than zero, then the integer part to
        be output has a single digit, which is nonzero except for the value
        0.0 of Item.
        25   In both cases, however, if the integer part to be output has
        fewer than Fore characters, including any minus sign, then leading
        spaces are first output to make up the difference.  The number of
        digits of the fractional part is given by Aft, or is one if Aft
        equals zero.  The value is rounded; a value of exactly one half in
        the last place is rounded away from zero.  {94-4932.a}
        26   If Exp has the value zero, there is no exponent part.  If Exp
        has a value greater than zero, then the exponent part to be output
        has as many digits as are needed to represent the exponent part of
        the value of Item (for which a single digit integer part is used),
        and includes an initial sign (plus or minus).  If the exponent part
        to be output has fewer than Exp characters, including the sign, then
        leading zeros precede the digits, to make up the difference.  For the
        value 0.0 of Item, the exponent has the value zero.


27  procedure Get(From : in String; Item : out Num; Last : out Positive);

        28   Reads a real value from the beginning of the given string,
        following the same rule as the Get procedure that reads a real value
        from a file, but treating the end of the string as a file terminator.
        Returns, in the parameter Item, the value of type Num that
        corresponds to the sequence input.  Returns in Last the index value
        such that From(Last) is the last character read.
        29   The exception Data_Error is propagated if the sequence input
        does not have the required syntax, or if the value obtained is not of
        the subtype Num.


30  procedure Put(To   : out String;
                  Item : in Num;
                  Aft  : in Field := Default_Aft;
                  Exp  : in Field := Default_Exp);

        31   Outputs the value of the parameter Item to the given string,
        following the same rule as for output to a file, using a value for
        Fore such that the sequence of characters output exactly fills the
        string, including any leading spaces.

32   Float_Text_IO is a library package that is a nongeneric equivalent to
Text_IO.Float_IO for the predefined type Float:

33  with Ada.Text_IO;
    package Ada.Float_Text_IO is new Ada.Text_IO.Float_IO(Float);

34   For each predefined floating point type, a nongeneric equivalent to
Text_IO.Float_IO is provided, with names such as Ada.Long_Float_Text_IO.

        34.a   Change:  Preinstantiations of Text_IO.Float_IO added, as per
        WG9 resolution.


                         Implementation Permissions

35   An implementation may extend Get [and Put] for floating point types to
support special values such as infinities and NaNs.  {94-4526.c} {94-4893.d}
{94-4901.a}

        35.a   Discussion:  See also the similar permission for the Wide_
        Value attribute in 3.5.

36   The implementation of Put need not produce an output value with greater
accuracy than is supported for the base subtype.  The additional accuracy, if
any, of the value produced by Put when the number of requested digits in the
integer and fractional parts exceeds the required accuracy is implementation
defined.  {94-4526.a}

        36.a   Discussion:  The required accuracy is thus Num'Base'Digits
        digits if Num is a floating point subtype.  For a fixed point subtype
        the required accuracy is a function of the subtype's Fore, Aft, and
        Delta attributes.

        36.b   Implementation defined:  The accuracy of the value produced by
        Put.

37   The nongeneric equivalent packages may, but need not, be actual
instantiations of the generic package for the appropriate predefined type.


     NOTES
38   (30) For an item with a positive value, if output to a string exactly
     fills the string without leading spaces, then output of the
     corresponding negative value will propagate Layout_Error.

39   (31) The rules for the Value attribute (see 3.5) and the rules for Get
     are based on the same set of formats.


                                  Examples

40

41  package Real_IO is new Float_IO(Real); use Real_IO;
    -- default format used at instantiation, Default_Exp = 3

42  X : Real := -123.4567;  --  digits 8      (see 3.5.7)

43
    Put(X);  -- default format                          "-1.2345670E+02"
    Put(X, Fore => 5, Aft => 3, Exp => 2);              -- "bbb-1.235E+2"
    Put(X, 5, 3, 0);                                    -- "b-123.457"



A.10.10 Input-Output for Enumeration Types

                              Static Semantics

1   The following procedures are defined in the generic package
Enumeration_IO, which has to be instantiated for the appropriate enumeration
type (indicated by Enum in the specification).

2   Values are output using either upper or lower case letters for
identifiers.  This is specified by the parameter Set, which is of the
enumeration type Type_Set.

3   type Type_Set is (Lower_Case, Upper_Case);

4   The format (which includes any trailing spaces) can be specified by an
optional field width parameter.  The default field width and letter case are
defined by the following variables that are declared in the generic package
Enumeration_IO:

5   Default_Width   : Field := 0;
    Default_Setting : Type_Set := Upper_Case;

6   The following procedures are provided:


7   procedure Get(File : in File_Type; Item : out Enum);
    procedure Get(Item : out Enum);

        8   After skipping any leading blanks, line terminators, or page
        terminators, reads an identifier according to the syntax of this
        lexical element (lower and upper case being considered equivalent),
        or a character literal according to the syntax of this lexical
        element (including the apostrophes).  Returns, in the parameter Item,
        the value of type Enum that corresponds to the sequence input.
        9   The exception Data_Error is propagated if the sequence input does
        not have the required syntax, or if the identifier or character
        literal does not correspond to a value of the subtype Enum.


10  procedure Put(File  : in File_Type;
                  Item  : in Enum;
                  Width : in Field := Default_Width;
                  Set   : in Type_Set := Default_Setting);

    procedure Put(Item  : in Enum;
                  Width : in Field := Default_Width;
                  Set   : in Type_Set := Default_Setting);

        11   Outputs the value of the parameter Item as an enumeration
        literal (either an identifier or a character literal).  The optional
        parameter Set indicates whether lower case or upper case is used for
        identifiers; it has no effect for character literals.  If the
        sequence of characters produced has fewer than Width characters, then
        trailing spaces are finally output to make up the difference.  If
        Enum is a character type, the sequence of characters produced is as
        for Enum'Image(Item), as modified by the Width and Set parameters.
        {94-4913.c}

        11.a   Discussion:  For a character type, the literal might be a
        Wide_Character or a control character.  Whatever Image does for these
        things is appropriate here, too.


12  procedure Get(From : in String; Item : out Enum; Last : out Positive);

        13   Reads an enumeration value from the beginning of the given
        string, following the same rule as the Get procedure that reads an
        enumeration value from a file, but treating the end of the string as
        a file terminator.  Returns, in the parameter Item, the value of type
        Enum that corresponds to the sequence input.  Returns in Last the
        index value such that From(Last) is the last character read.
        14   The exception Data_Error is propagated if the sequence input
        does not have the required syntax, or if the identifier or character
        literal does not correspond to a value of the subtype Enum.

        14.a   To be honest:  For a character type, it is permissible for the
        implementation to make Get do the inverse of what Put does, in the
        case of wide character_literals and control characters.


15  procedure Put(To   : out String;
                  Item : in Enum;
                  Set  : in Type_Set := Default_Setting);

        16   Outputs the value of the parameter Item to the given string,
        following the same rule as for output to a file, using the length of
        the given string as the value for Width.

17   Although the specification of the generic package Enumeration_IO would
allow instantiation for an float type, this is not the intended purpose of
this generic package, and the effect of such instantiations is not defined by
the language.


     NOTES
18   (32) There is a difference between Put defined for characters, and for
     enumeration values.  Thus

19       Ada.Text_IO.Put('A');  --  outputs the character A

20       package Char_IO is new Ada.Text_IO.Enumeration_IO(Character);
         Char_IO.Put('A');  --  outputs the character 'A', between apostrophes

21   (33) The type Boolean is an enumeration type, hence Enumeration_IO can
     be instantiated for this type.



A.11 Wide Text Input-Output

1   The package Wide_Text_IO provides facilities for input and output in
human-readable form.  Each file is read or written sequentially, as a
sequence of wide characters grouped into lines, and as a sequence of lines
grouped into pages.


                              Static Semantics

2   {Ada.Wide_Text_IO} The specification of package Wide_Text_IO is the same
as that for Text_IO, except that in each Get, Look_Ahead, Get_Immediate, Get_
Line, Put, and Put_Line procedure, any occurrence of Character is replaced by
Wide_Character, and any occurrence of String is replaced by Wide_String.

3   {Ada.Integer_Wide_Text_IO} {Ada.Float_Wide_Text_IO} Nongeneric equiv-
alents of Wide_Text_IO.Integer_IO and Wide_Text_IO.Float_IO are provided (as
for Text_IO) for each predefined numeric type, with names such as
Ada.Integer_Wide_Text_IO, Ada.Long_Integer_Wide_Text_IO, Ada.Float_Wide_
Text_IO, Ada.Long_Float_Wide_Text_IO.

        3.a   Change:  Preinstantiations of Wide_Text_IO.Integer_IO and Wide_
        Text_IO.Float_IO added, as per WG9 resolution.


                            Extensions to Ada 83

        3.b   {extensions to Ada 83} Support for Wide_Character and Wide_
        String I/O is new in Ada 9X.



A.12 Stream Input-Output

1   The packages Streams.Stream_IO, Text_IO.Text_Streams, and Wide_
Text_IO.Text_Streams provide stream-oriented operations on files.
{94-4817.a}



A.12.1 The Package Streams.Stream_IO

1   {heterogeneous input-output} [The subprograms in the child package
Streams.Stream_IO provide control over stream files.  Access to a stream file
is either sequential, via a call on Read or Write to transfer an array of
stream elements, or positional (if supported by the implementation for the
given file), by specifying a relative index for an element.  Since a stream
file can be converted to a Stream_Access value, calling stream-oriented
attribute subprograms of different element types with the same Stream_Access
value provides heterogeneous input-output.]  See 13.13 for a general
discussion of streams.


                              Static Semantics

2   The library package Streams.Stream_IO has the following declaration:

3   with Ada.IO_Exceptions;
    package Ada.Streams.Stream_IO is

4       type Stream_Access is access all Root_Stream_Type'Class;

5       type File_Type is limited private;

6       type File_Mode is (In_File, Out_File, Append_File);

7       type    Count          is range 0 .. implementation-defined;
        subtype Positive_Count is Count range 1 .. Count'Last;
          -- Index into file, in stream elements.

8       procedure Create (File : in out File_Type;
                          Mode : in File_Mode := Out_File;
                          Name : in String    := "";
                          Form : in String    := "");

9       procedure Open (File : in out File_Type;
                        Mode : in File_Mode;
                        Name : in String;
                        Form : in String := "");

10      procedure Close  (File : in out File_Type);
        procedure Delete (File : in out File_Type);
        procedure Reset  (File : in out File_Type; Mode : in File_Mode);
        procedure Reset  (File : in out File_Type);

11      function Mode (File : in File_Type) return File_Mode;
        function Name (File : in File_Type) return String;
        function Form (File : in File_Type) return String;

12      function Is_Open     (File : in File_Type) return Boolean;
        function End_Of_File (File : in File_Type) return Boolean;

13      function Stream (File : in File_Type) return Stream_Access;
            -- Return stream access for use with T'Input and T'Output

14


15      -- Read array of stream elements from file
        procedure Read (File : in  File_Type;
                        Item : out Stream_Element_Array;
                        Last : out Stream_Element_Offset;
                        From : in  Positive_Count);

16      procedure Read (File : in  File_Type;
                        Item : out Stream_Element_Array;
                        Last : out Stream_Element_Offset);

17


18      -- Write array of stream elements into file
        procedure Write (File : in File_Type;
                         Item : in Stream_Element_Array;
                         To   : in Positive_Count);

19      procedure Write (File : in File_Type;
                               Item : in Stream_Element_Array);

20


21      -- Operations on position within file

22      procedure Set_Index(File : in File_Type; To : in Positive_Count);

23      function Index(File : in File_Type) return Positive_Count;
        function Size (File : in File_Type) return Count;

24      procedure Set_Mode(File : in out File_Type; Mode : in File_Mode);

25      procedure Flush(File : in out File_Type);

26      -- exceptions
        Status_Error : exception renames IO_Exceptions.Status_Error;
        Mode_Error   : exception renames IO_Exceptions.Mode_Error;
        Name_Error   : exception renames IO_Exceptions.Name_Error;
        Use_Error    : exception renames IO_Exceptions.Use_Error;
        Device_Error : exception renames IO_Exceptions.Device_Error;
        End_Error    : exception renames IO_Exceptions.End_Error;
        Data_Error   : exception renames IO_Exceptions.Data_Error;

27  private
       ... -- not specified by the language
    end Ada.Streams.Stream_IO;

{94-4757.a} {94-4770.a} {94-4819.a}

28   The subprograms Create, Open, Close, Delete, Reset, Mode, Name, Form,
Is_Open, and End_of_File have the same effect as the corresponding
subprograms in Sequential_IO (see A.8.2).

29   The Stream function returns a Stream_Access result from a File_Type
object, thus allowing the stream-oriented attributes Read, Write, Input, and
Output to be used on the same file for multiple types.

30   The procedures Read and Write are equivalent to the corresponding
operations in the package Streams.  Read propagates Mode_Error if the mode of
File is not In_File.  Write propagates Mode_Error if the mode of File is not
Out_File or Append_File.  The Read procedure with a Positive_Count parameter
starts reading at the specified index.  The Write procedure with a Positive_
Count parameter starts writing at the specified index.

31   The Index function returns the current file index, as a count (in stream
elements) from the beginning of the file.  The position of the first element
in the file is 1.

        31.a   Ramification:  The notion of Index for Stream_IO is analogous
        to that of Index in Direct_IO, except that the former is measured in
        Stream_Element units, whereas the latter is in terms of Element_Type
        values.

32   The Set_Index procedure sets the current index to the specified value.

33   If positioning is not supported for the given file, then a call of Index
or Set_Index propagates Use_Error.  Similarly, a call of Read or Write with a
Positive_Count parameter propagates Use_Error.

34   The Size function returns the current size of the file, in stream
elements.

35   The Set_Mode procedure changes the mode of the file.  If the new mode is
Append_File, the file is positioned to its end; otherwise, the position in
the file is unchanged.

36   The Flush procedure synchronizes the external file with the internal
file (by flushing any internal buffers) without closing the file or changing
the position.  Mode_Error is propagated if the mode of the file is In_File.



A.12.2 The Package Text_IO.Text_Streams

1   The package Text_IO.Text_Streams provides a function for treating a text
file as a stream.


                              Static Semantics

2   The library package Text_IO.Text_Streams has the following declaration:

3   with Ada.Streams;
    package Ada.Text_IO.Text_Streams is
       type Stream_Access is access all Streams.Root_Stream_Type'Class;

4      function Stream (File : in File_Type) return Stream_Access;
    end Ada.Text_IO.Text_Streams;

5   The Stream function has the same effect as the corresponding function in
Streams.Stream_IO.


     NOTES
6    (34) The ability to obtain a stream for a text file allows Current_
     Input, Current_Output, and Current_Error to be processed with the
     functionality of streams, including the mixing of text and binary
     input-output, and the mixing of binary input-output for different types.

7    (35) Performing operations on the stream associated with a text file
     does not affect the column, line, or page counts.



A.12.3 The Package Wide_Text_IO.Text_Streams

1   The package Wide_Text_IO.Text_Streams provides a function for treating a
wide text file as a stream.


                              Static Semantics

2   The library package Wide_Text_IO.Text_Streams has the following
declaration:

3   with Ada.Streams;
    package Ada.Wide_Text_IO.Text_Streams is
       type Stream_Access is access all Streams.Root_Stream_Type'Class;

4      function Stream (File : in File_Type) return Stream_Access;
    end Ada.Wide_Text_IO.Text_Streams;

5   The Stream function has the same effect as the corresponding function in
Streams.Stream_IO.


{94-4817.a}



A.13 Exceptions in Input-Output

1   The package IO_Exceptions defines the exceptions needed by the predefined
input-output packages.


                              Static Semantics

2   The library package IO_Exceptions has the following declaration:

3   package Ada.IO_Exceptions is
       pragma Pure(IO_Exceptions);

4      Status_Error : exception;
       Mode_Error   : exception;
       Name_Error   : exception;
       Use_Error    : exception;
       Device_Error : exception;
       End_Error    : exception;
       Data_Error   : exception;
       Layout_Error : exception;

5   end Ada.IO_Exceptions;

6   If more than one error condition exists, the corresponding exception that
appears earliest in the following list is the one that is propagated.

7   The exception Status_Error is propagated by an attempt to operate upon a
file that is not open, and by an attempt to open a file that is already open.

8   The exception Mode_Error is propagated by an attempt to read from, or
test for the end of, a file whose current mode is Out_File or Append_File,
and also by an attempt to write to a file whose current mode is In_File.  In
the case of Text_IO, the exception Mode_Error is also propagated by
specifying a file whose current mode is Out_File or Append_File in a call of
Set_Input, Skip_Line, End_Of_Line, Skip_Page, or End_Of_Page; and by
specifying a file whose current mode is In_File in a call of Set_Output, Set_
Line_Length, Set_Page_Length, Line_Length, Page_Length, New_Line, or New_
Page.

9   The exception Name_Error is propagated by a call of Create or Open if the
string given for the parameter Name does not allow the identification of an
external file.  For example, this exception is propagated if the string is
improper, or, alternatively, if either none or more than one external file
corresponds to the string.

10   The exception Use_Error is propagated if an operation is attempted that
is not possible for reasons that depend on characteristics of the external
file.  For example, this exception is propagated by the procedure Create,
among other circumstances, if the given mode is Out_File but the form
specifies an input only device, if the parameter Form specifies invalid
access rights, or if an external file with the given name already exists and
overwriting is not allowed.

11   The exception Device_Error is propagated if an input-output operation
cannot be completed because of a malfunction of the underlying system.

12   The exception End_Error is propagated by an attempt to skip (read past)
the end of a file.

13   The exception Data_Error can be propagated by the procedure Read (or by
the Read attribute) if the element read cannot be interpreted as a value of
the required subtype.  This exception is also propagated by a procedure Get
(defined in the package Text_IO) if the input character sequence fails to
satisfy the required syntax, or if the value input does not belong to the
range of the required subtype.

14   The exception Layout_Error is propagated (in text input-output) by Col,
Line, or Page if the value returned exceeds Count'Last.  The exception
Layout_Error is also propagated on output by an attempt to set column or line
numbers in excess of specified maximum line or page lengths, respectively
(excluding the unbounded cases).  It is also propagated by an attempt to Put
too many characters to a string.


                         Documentation Requirements

15   {documentation requirements} The implementation shall document the
conditions under which Name_Error, Use_Error and Device_Error are propagated.


{94-4761.o}

                         Implementation Permissions

16   If the associated check is too complex, an implementation need not
propagate Data_Error as part of a procedure Read (or the Read attribute) if
the value read cannot be interpreted as a value of the required subtype.

        16.a   Ramification:  An example where the implementation may choose
        not to perform the check is an enumeration type with a representation
        clause with ``holes'' in the range of internal codes.


                             Erroneous Execution

17   {erroneous execution} [If the element read by the procedure Read (or by
the Read attribute) cannot be interpreted as a value of the required subtype,
but this is not detected and Data_Error is not propagated, then the resulting
value can be abnormal, and subsequent references to the value can lead to
erroneous execution, as explained in 13.9.1.  {normal state of an object
[partial]} {abnormal state of an object [partial]} ]



A.14 File Sharing

                              Dynamic Semantics

1   {unspecified [partial]} It is not specified by the language whether the
same external file can be associated with more than one file object.  If such
sharing is supported by the implementation, the following effects are
defined:

    2  Operations on one text file object do not affect the column,
       line, and page numbers of any other file object.

    3  Standard_Input and Standard_Output are associated with distinct
       external files, so operations on one of these files cannot affect
       operations on the other file.  In particular, reading from
       Standard_Input does not affect the current page, line, and column
       numbers for Standard_Output, nor does writing to Standard_Output
       affect the current page, line, and column numbers for Standard_
       Input.

    4  For direct and stream files, the current index is a property of
       each file object; an operation on one file object does not affect
       the current index of any other file object.

    5  For direct and stream files, the current size of the file is a
       property of the external file.

6   All other effects are identical.



A.15 The Package Command_Line

1   The package Command_Line allows a program to obtain the values of its
arguments and to set the exit status code to be returned on normal
termination.

        1.a   Implementation defined:  The meaning of Argument_Count,
        Argument, and Command_Name.


                              Static Semantics

2   The library package Ada.Command_Line has the following declaration:

3   package Ada.Command_Line is
      pragma Preelaborate(Command_Line);

4     function Argument_Count return Natural;

5     function Argument (Number : in Positive) return String;

6     function Command_Name return String;

7     type Exit_Status is implementation-defined integer type;

8     Success : constant Exit_Status;
      Failure : constant Exit_Status;

9     procedure Set_Exit_Status (Code : in Exit_Status);

10  private
      ... -- not specified by the language
    end Ada.Command_Line;

{94-4758.a} {94-4976.a}


11  function Argument_Count return Natural;

        12   If the external execution environment supports passing arguments
        to a program, then Argument_Count returns the number of arguments
        passed to the program invoking the function.  Otherwise it returns 0.
        The meaning of ``number of arguments'' is implementation defined.


13  function Argument (Number : in Positive) return String;

        14   If the external execution environment supports passing arguments
        to a program, then Argument returns an implementation-defined value
        corresponding to the argument at relative position Number.
        {Constraint_Error (raised by failure of run-time check)} If Number is
        outside the range 1..Argument_Count, then Constraint_Error is
        propagated.

        14.a   Ramification:  If the external execution environment does not
        support passing arguments to a program, then Argument(N) for any N
        will raise Constraint_Error, since Argument_Count is 0.


15  function Command_Name return String;

        16   If the external execution environment supports passing arguments
        to a program, then Command_Name returns an implementation-defined
        value corresponding to the name of the command invoking the program;
        otherwise Command_Name returns the null string.
        17   The type Exit_Status represents the range of exit status values
        supported by the external execution environment.  The constants
        Success and Failure correspond to success and failure, respectively.


18  procedure Set_Exit_Status (Code : in Exit_Status);

        19   If the external execution environment supports returning an exit
        status from a program, then Set_Exit_Status sets Code as the status.
        Normal termination of a program returns as the exit status the value
        most recently set by Set_Exit_Status, or, if no such value has been
        set, then the value Success.  If a program terminates abnormally, the
        status set by Set_Exit_Status is ignored, and an implementation-
        defined exit status value is set.
        20   {unspecified [partial]} If the external execution environment
        does not support returning an exit value from a program, then Set_
        Exit_Status does nothing.  {94-4984.a}


                         Implementation Permissions

21   An alternative declaration is allowed for package Command_Line if
different functionality is appropriate for the external execution
environment.


     NOTES
22   (36) Argument_Count, Argument, and Command_Name correspond to the C
     language's argc, argv[n] (for n>0) and argv[0], respectively.


                            Extensions to Ada 83

        22.a   {extensions to Ada 83} This clause is new in Ada 9X.



                                   Annex B
                                 (normative)


                         Interface to Other Languages



1   {interface to other languages} {language (interface to non-Ada)}
{mixed-language programs} This Annex describes features for writing
mixed-language programs.  General interface support is presented first; then
specific support for C, COBOL, and Fortran is defined, in terms of language
interface packages for each of these languages.

        1.a   Ramification:  This Annex is not a ``Specialized Needs'' annex.
        Every implementation must support all non-optional features defined
        here (mainly the package Interfaces).


                         Language Design Principles

        1.b   Ada should have strong support for mixed-language programming.

                            Extensions to Ada 83

        1.c   {extensions to Ada 83} Much of the functionality in this Annex
        is new to Ada 9X.

                         Wording Changes From Ada 83

        1.d   This Annex contains what used to be RM83-13.8.



B.1 Interfacing Pragmas

1   A pragma Import is used to import an entity defined in a foreign language
into an Ada program, thus allowing a foreign-language subprogram to be called
from Ada, or a foreign-language variable to be accessed from Ada.  In
contrast, a pragma Export is used to export an Ada entity to a foreign
language, thus allowing an Ada subprogram to be called from a foreign
language, or an Ada object to be accessed from a foreign language.  The
pragmas Import and Export are intended primarily for objects and subprograms,
although implementations are allowed to support other entities.

2   A pragma Convention is used to specify that an Ada entity should use the
conventions of another language.  It is intended primarily for types and
``callback'' subprograms.  For example, ``pragma Convention(Fortran,
Matrix);'' implies that Matrix should be represented according to the
conventions of the supported Fortran implementation, namely column-major
order.

3   A pragma Linker_Options is used to specify the system linker parameters
needed when a given compilation unit is included in a partition.


                                   Syntax

    4   {interfacing pragma [distributed]} {interfacing pragma [Import]}
    {pragma, interfacing [Import]} {interfacing pragma [Export]} {pragma,
    interfacing [Export]} {interfacing pragma [Convention]} {pragma,
    interfacing [Convention]} {pragma, interfacing [Linker_Options]} An
    interfacing pragma is a representation pragma that is one of the pragmas
    Import, Export, or Convention.  Their forms, together with that of the
    related pragma Linker_Options, are as follows:


5     pragma Import(
          [Convention =>] convention_identifier, [Entity =>] local_name
       [, [External_Name =>] string_expression] [, [Link_Name =>] string_expres\
sion]);

6     pragma Export(
          [Convention =>] convention_identifier, [Entity =>] local_name
       [, [External_Name =>] string_expression] [, [Link_Name =>] string_expres\
sion]);

7     pragma Convention([Convention =>] convention_identifier,[Entity =>] local\
_name);

8     pragma Linker_Options(string_expression);

    9   A pragma Linker_Options is allowed only at the place of a
    declarative_item.


                            Name Resolution Rules

10   {expected type [link name]} The expected type for a string_expression in
an interfacing pragma or in pragma Linker_Options is String.

        10.a   Ramification:  There is no language-defined support for
        external or link names of type Wide_String, or of other string types.
        Implementations may, of course, have additional pragmas for that
        purpose.  Note that allowing both String and Wide_String in the same
        pragma would cause ambiguities.


                               Legality Rules

11   {convention} The convention_identifier of an interfacing pragma shall be
the name of a convention.  The convention names are implementation defined,
except for certain language-defined ones, such as Ada and Intrinsic, as
explained in 6.3.1, ``Conformance Rules''.  [Additional convention names
generally represent the calling conventions of foreign languages, language
implementations, or specific run-time models.]  {calling convention} The
convention of a callable entity is its calling convention.

        11.a   Implementation defined:  Implementation-defined convention
        names.

        11.b   Discussion:  We considered representing the convention names
        using an enumeration type declared in System.  Then,
        convention_identifier would be changed to convention_name, and we
        would make its expected type be the enumeration type.  We didn't do
        this because it seems to introduce extra complexity, and because the
        list of available languages is better represented as the list of
        children of package Interfaces -- a more open-ended sort of list.

12   {compatible (a type, with a convention)} If L is a convention_identifier
for a language, then a type T is said to be compatible with convention L,
(alternatively, is said to be an L-compatible type) if any of the following
conditions are met:

   13  T is declared in a language interface package corresponding to L
       and is defined to be L-compatible (see B.3, B.3.1, B.3.2, B.4,
       B.5),

   14  {eligible (a type, for a convention)} Convention L has been
       specified for T in a pragma Convention, and T is eligible for
       convention L; that is:

          15  T is an array type with either an unconstrained or
              statically-constrained first subtype, and its component
              type is L-compatible,

          16  T is a record type that has no discriminants and that only
              has components with statically-constrained subtypes, and
              each component type is L-compatible,

          17  T is an access-to-object type, and its designated type is
              L-compatible,

          18  T is an access-to-subprogram type, and its designated
              profile's parameter and result types are all L-compatible.

   19  T is derived from an L-compatible type,

   20  The implementation permits T as an L-compatible type.

 20.a   Discussion:  For example, an implementation might permit Integer
        as a C-compatible type, though the C type to which it
        corresponds might be different in different environments.

21   If pragma Convention applies to a type, then the type shall either be
compatible with or eligible for the convention specified in the pragma.

        21.a   Ramification:  If a type is derived from an L-compatible type,
        the derived type is by default L-compatible, but it is also permitted
        to specify pragma Convention for the derived type.

        21.b   It is permitted to specify pragma Convention for an incomplete
        type, but in the complete declaration each component must be
        L-compatible.

        21.c   If each component of a record type is L-compatible, then the
        record type itself is only L-compatible if it has a pragma
        Convention.

22   A pragma Import shall be the completion of a declaration.
{notwithstanding} Notwithstanding any rule to the contrary, a pragma Import
may serve as the completion of any kind of (explicit) declaration if
supported by an implementation for that kind of declaration.  If a completion
is a pragma Import, then it shall appear in the same declarative_part,
package_specification, task_definition or protected_definition as the
declaration.  For a library unit, it shall appear in the same compilation,
before any subsequent compilation_units other than pragmas.  If the local_
name denotes more than one entity, then the pragma Import is the completion
of all of them.

        22.a   Discussion:  For declarations of deferred constants and
        subprograms, we mention pragma Import explicitly as a possible
        completion.  For other declarations that require completions, we
        ignore the possibility of pragma Import.  Nevertheless, if an
        implementation chooses to allow a pragma Import to complete the
        declaration of a task, protected type, incomplete type, private type,
        etc., it may do so, and the normal completion is then not allowed for
        that declaration.

23   {imported entity} {exported entity} An entity specified as the Entity
argument to a pragma Import (or pragma Export) is said to be imported
(respectively, exported).

24   The declaration of an imported object shall not include an explicit
initialization expression.  [Default initializations are not performed.]

        24.a   Proof:  This follows from the ``Notwithstanding ...''  wording
        in the Dynamics Semantics paragraphs below.

25   The type of an imported or exported object shall be compatible with the
convention specified in the corresponding pragma.

        25.a   Ramification:  This implies, for example, that importing an
        Integer object might be illegal, whereas importing an object of type
        Interfaces.C.int would be permitted.

26   For an imported or exported subprogram, the result and parameter types
shall each be compatible with the convention specified in the corresponding
pragma.

27   The external name and link name string_expressions of a pragma Import or
Export, and the string_expression of a pragma Linker_Options, shall be
static.
                              Static Semantics

28   {representation pragma [Import]} {pragma, representation [Import]}
{representation pragma [Export]} {pragma, representation [Export]}
{representation pragma [Convention]} {pragma, representation [Convention]}
{aspect of representation [convention, calling convention]} {convention
(aspect of representation)} Import, Export, and Convention pragmas are
representation pragmas that specify the convention aspect of representation.
{aspect of representation [imported]} {imported (aspect of representation)}
{aspect of representation [exported]} {exported (aspect of representation)}
In addition, Import and Export pragmas specify the imported and exported
aspects of representation, respectively.

29   {program unit pragma [Import]} {pragma, program unit [Import]} {program
unit pragma [Export]} {pragma, program unit [Export]} {program unit pragma
[Convention]} {pragma, program unit [Convention]} An interfacing pragma is a
program unit pragma when applied to a program unit (see 10.1.5).

30   An interfacing pragma defines the convention of the entity denoted by
the local_name.  The convention represents the calling convention or
representation convention of the entity.  For an access-to-subprogram type,
it represents the calling convention of designated subprograms.  In addition:

   31  A pragma Import specifies that the entity is defined externally
       (that is, outside the Ada program).

   32  A pragma Export specifies that the entity is used externally.

   33  A pragma Import or Export optionally specifies an entity's
       external name, link name, or both.

34   {external name} An external name is a string value for the name used by
a foreign language program either for an entity that an Ada program imports,
or for referring to an entity that an Ada program exports.

35   {link name} A link name is a string value for the name of an exported or
imported entity, based on the conventions of the foreign language's compiler
in interfacing with the system's linker tool.

36   The meaning of link names is implementation defined.

        36.a   Implementation defined:  The meaning of link names.

        36.b   Ramification:  For example, an implementation might always
        prepend "_", and then pass it to the system linker.

If neither a link name nor the Address attribute of an imported or exported
entity is specified, then a link name is chosen in an implementation-defined
manner, based on the external name if one is specified.

        36.c   Implementation defined:  The manner of choosing link names
        when neither the link name nor the address of an imported or exported
        entity is specified.

        36.d   Ramification:  Normally, this will be the entity's defining
        name, or some simple transformation thereof.

37   Pragma Linker_Options has the effect of passing its string argument as a
parameter to the system linker (if one exists), if the immediately enclosing
compilation unit is included in the partition being linked.  The
interpretation of the string argument, and the way in which the string
arguments from multiple Linker_Options pragmas are combined, is
implementation defined.

        37.a   Implementation defined:  The effect of pragma Linker_Options.


                              Dynamic Semantics

38   {elaboration [declaration named by a pragma Import]} {notwithstanding}
Notwithstanding what this International Standard says elsewhere, the
elaboration of a declaration denoted by the local_name of a pragma Import
does not create the entity.  Such an elaboration has no other effect than to
allow the defining name to denote the external entity.

        38.a   Ramification:  This implies that default initializations are
        skipped.  (Explicit initializations are illegal.)  For example, an
        imported access object is not initialized to null.

        38.b   Note that the local_name in a pragma Import might denote more
        than one declaration; in that case, the entity of all of those
        declarations will be the external entity.

        38.c   Discussion:  This ``notwithstanding'' wording is better than
        saying ``unless named by a pragma Import'' on every definition of
        elaboration.  It says we recognize the contradiction, and this rule
        takes precedence.


                            Implementation Advice

39   If an implementation supports pragma Export to a given language, then it
should also allow the main subprogram to be written in that language.  It
should support some mechanism for invoking the elaboration of the Ada library
units included in the system, and for invoking the finalization of the
environment task.  On typical systems, the recommended mechanism is to
provide two subprograms whose link names are "adainit" and "adafinal".
Adainit should contain the elaboration code for library units.  Adafinal
should contain the finalization code.  These subprograms should have no
effect the second and subsequent time they are called.

        39.a   Ramification:  For example, if the main subprogram is written
        in C, it can call adainit before the first call to an Ada subprogram,
        and adafinal after the last.

40   Automatic elaboration of preelaborated packages should be provided when
pragma Export is supported.

41   For each supported convention L other than Intrinsic, an implementation
should support Import and Export pragmas for objects of L-compatible types
and for subprograms, and pragma Convention for L-eligible types and for
subprograms, presuming the other language has corresponding features.  Pragma
Convention need not be supported for scalar types.

        41.a   Reason:  Pragma Convention is not necessary for scalar types,
        since the language interface packages declare scalar types
        corresponding to those provided by the respective foreign languages.

        41.b   Implementation Note:  If an implementation supports
        interfacing to C++, it should do so via the convention identifier C_
        Plus_Plus (in additional to any C++-implementation-specific ones).

        41.c   Reason:  The reason for giving the advice about C++ is to
        encourage uniformity among implementations, given that the name of
        the language is not syntactically legal as an identifier.  We place
        this advice in the AARM, rather than the RM9X proper, because (as of
        this writing) C++ is not an international standard, and we don't want
        to refer to a such a language from an international standard.


     NOTES
42   (1) Implementations may place restrictions on interfacing pragmas; for
     example, requiring each exported entity to be declared at the library
     level.

   42.a   Proof:  Arbitrary restrictions are allowed by 13.1.

   42.b   Ramification:  Such a restriction might be to disallow them
        altogether.  Alternatively, the implementation might allow them only
        for certain kinds of entities, or only for certain conventions.

43   (2) A pragma Import specifies the conventions for accessing external
     entities.  It is possible that the actual entity is written in assembly
     language, but reflects the conventions of a particular language.  For
     example, pragma Import(Ada, ...) can be used to interface to an assembly
     language routine that obeys the Ada compiler's calling conventions.

44   (3) To obtain ``call-back'' to an Ada subprogram from a foreign language
     environment, pragma Convention should be specified both for the
     access-to-subprogram type and the specific subprogram(s) to which
     'Access is applied.

45   (4) It is illegal to specify more than one of Import, Export, or
     Convention for a given entity.

46   (5) The local_name in an interfacing pragma can denote more than one
     entity in the case of overloading.  Such a pragma applies to all of the
     denoted entities.

47   (6) See also 13.8, ``Machine Code Insertions''.

   47.a   Ramification:  The Intrinsic convention (see 6.3.1) implies that
        the entity is somehow ``built in'' to the implementation.  Thus, it
        generally does not make sense for users to specify Intrinsic in a
        pragma Import.  The intention is that only implementations will
        specify Intrinsic in a pragma Import.  The language also defines
        certain subprograms to be Intrinsic.

   47.b   Discussion:  There are many imaginable interfacing pragmas that
        don't make any sense.  For example, setting the Convention of a
        protected procedure to Ada is probably wrong.  Rather than
        enumerating all such cases, however, we leave it up to
        implementations to decide what is sensible.

48   (7) If both External_Name and Link_Name are specified for an Import or
     Export pragma, then the External_Name is ignored.

49   (8) An interfacing pragma might result in an effect that violates Ada
     semantics.


                                  Examples

50   Example of interfacing pragmas:

51  package Fortran_Library is
      function Sqrt (X : Float) return Float;
      function Exp  (X : Float) return Float;
    private
      pragma Import(Fortran, Sqrt);
      pragma Import(Fortran, Exp);
    end Fortran_Library;


                            Extensions to Ada 83

        51.a   {extensions to Ada 83} Interfacing pragmas are new to Ada 9X.
        Pragma Import replaces Ada 83's pragma Interface.  Existing
        implementations can continue to support pragma Interface for upward
        compatibility.
B.2 The Package Interfaces

1   Package Interfaces is the parent of several library packages that declare
types and other entities useful for interfacing to foreign languages.  It
also contains some implementation-defined types that are useful across more
than one language (in particular for interfacing to assembly language).

        1.a   Implementation defined:  The contents of the visible part of
        package Interfaces and its language-defined descendants.


                              Static Semantics

2   The library package Interfaces has the following skeletal declaration:

3   package Interfaces is
       pragma Pure(Interfaces);

4      type Integer_n is range -2**(n-1) .. 2**(n-1) - 1;  --2's complement{94-\
4816.a}

5      type Unsigned_n is mod 2**n;

6      function Shift_Left  (Value : Unsigned_n; Amount : Natural) return Unsig\
ned_n;
       function Shift_Right (Value : Unsigned_n; Amount : Natural) return Unsig\
ned_n;
       function Shift_Right_Arithmetic (Value : Unsigned_n; Amount : Natural)
          return Unsigned_n;
       function Rotate_Left  (Value : Unsigned_n; Amount : Natural) return Unsi\
gned_n;
       function Rotate_Right (Value : Unsigned_n; Amount : Natural) return Unsi\
gned_n;
       ...
    end Interfaces;


                         Implementation Requirements

7   An implementation shall provide the following declarations in the visible
part of package Interfaces:

    8  Signed and modular integer types of n bits, if supported by the
       target architecture, for each n that is at least the size of a
       storage element and that is a factor of the word size.  The names
       of these types are of the form Integer_n for the signed types,
       and Unsigned_n for the modular types;

 8.a    Ramification:  For example, for a typical 32-bit machine the
        corresponding types might be Integer_8, Unsigned_8, Integer_16,
        Unsigned_16, Integer_32, and Unsigned_32.

 8.b    The wording above implies, for example, that Integer_16'Size =
        Unsigned_16'Size = 16.  Unchecked conversions between same-Sized
        types will work as expected.

    9  {shift} {rotate} For each such modular type in Interfaces,
       shifting and rotating subprograms as specified in the declaration
       of Interfaces above.  These subprograms are Intrinsic.  They
       operate on a bit-by-bit basis, using the binary representation of
       the value of the operands to yield a binary representation for
       the result.  The Amount parameter gives the number of bits by
       which to shift or rotate.  For shifting, zero bits are shifted
       in, except in the case of Shift_Right_Arithmetic, where one bits
       are shifted in if Value is at least half the modulus.

        9.a   Reason:  We considered making shifting and rotating be
        primitive operations of all modular types.  However, it is a
        design principle of Ada that all predefined operations should be
        operators (not functions named by identifiers).  (Note that an
        early version of Ada had "abs" as an identifier, but it was
        changed to a reserved word operator before standardization of
        Ada 83.)  This is important because the implicit declarations
        would hide non-overloadable declarations with the same name,
        whereas operators are always overloadable.  Therefore, we would
        have had to make shift and rotate into reserved words, which
        would have been upward incompatible, or else invent new operator
        symbols, which seemed like too much mechanism.

   10  Floating point types corresponding to each floating point format
       fully supported by the hardware.

 10.a   Implementation Note:  The names for these floating point types
        are not specified.  {IEEE floating point arithmetic} However, if
        IEEE arithmetic is supported, then the names should be IEEE_
        Float_32 and IEEE_Float_64 for single and double precision,
        respectively.  {94-4438.a} {94-4889.q}


                         Implementation Permissions

11   An implementation may provide implementation-defined library units that
are children of Interfaces, and may add declarations to the visible part of
Interfaces in addition to the ones defined above.

        11.a   Implementation defined:  Implementation-defined children of
        package Interfaces.  The contents of the visible part of package
        Interfaces.


                            Implementation Advice

12   For each implementation-defined convention identifier, there should be a
child package of package Interfaces with the corresponding name.  This
package should contain any declarations that would be useful for interfacing
to the language (implementation) represented by the convention.  Any
declarations useful for interfacing to any language on the given hardware
architecture should be provided directly in Interfaces.

        12.a   Ramification:  For example, package Interfaces.XYZ_Pascal
        might contain declarations of types that match the data types
        provided by the XYZ implementation of Pascal, so that it will be more
        convenient to pass parameters to a subprogram whose convention is
        XYZ_Pascal.

13   An implementation supporting an interface to C, COBOL, or Fortran should
provide the corresponding package or packages described in the following
clauses.

        13.a   Implementation Note:  The intention is that an implementation
        might support several implementations of the foreign language:
        Interfaces.This_Fortran and Interfaces.That_Fortran might both exist.
        The ``default'' implementation, overridable by the user, should be
        declared as a renaming:

13.b        package Interfaces.Fortran renames Interfaces.This_Fortran;



B.3 Interfacing with C

1   {interface to C} {C interface} The facilities relevant to interfacing
with the C language are the package Interfaces.C and its children; and
support for the Import, Export, and Convention pragmas with
convention_identifier C.

2   The package Interfaces.C contains the basic types, constants and
subprograms that allow an Ada program to pass scalars and strings to C
functions.


                              Static Semantics

3   The library package Interfaces.C has the following declaration:

4   package Interfaces.C is
       pragma Pure(C);

5      -- Declarations based on C's <limits.h>

6      CHAR_BIT  : constant := implementation-defined;  -- typically 8
       SCHAR_MIN : constant := implementation-defined;  -- typically -128
       SCHAR_MAX : constant := implementation-defined;  -- typically 127
       UCHAR_MAX : constant := implementation-defined;  -- typically 255

7      -- Signed and Unsigned Integers
       type int   is range implementation-defined;
       type short is range implementation-defined;
       type long  is range implementation-defined;

8      type signed_char is range SCHAR_MIN .. SCHAR_MAX;
       for signed_char'Size use CHAR_BIT;

9      type unsigned       is mod implementation-defined;
       type unsigned_short is mod implementation-defined;
       type unsigned_long  is mod implementation-defined;

10     type unsigned_char is mod (UCHAR_MAX+1);
       for unsigned_char'Size use CHAR_BIT;

11     subtype plain_char is implementation-defined;

12     type ptrdiff_t is range implementation-defined;

13     type size_t is mod implementation-defined;

14     -- Floating Point

15     type C_float     is digits implementation-defined;

16     type double      is digits implementation-defined;

17     type long_double is digits implementation-defined;

18     -- Characters and Strings

19     type char is <implementation-defined character type>;

20     nul : constant char := char'First;

21     function To_C   (Item : in Character) return char;

22     function To_Ada (Item : in char) return Character;

23     type char_array is array (size_t range <>) of aliased char;
       pragma Pack(char_array);
       for char_array'Component_Size use CHAR_BIT;

24     function Is_Nul_Terminated (Item : in char_array) return Boolean;

25     function To_C   (Item       : in String;
                        Append_Nul : in Boolean := True)
          return char_array;

26     function To_Ada (Item     : in char_array;
                        Trim_Nul : in Boolean := True)
          return String;

27     procedure To_C (Item       : in String;
                       Target     : out char_array;
                       Count      : out size_t;
                       Append_Nul : in Boolean := True);

28     procedure To_Ada (Item     : in char_array;
                         Target   : out String;
                         Count    : out Natural;
                         Trim_Nul : in Boolean := True);

29     -- Wide Character and Wide String

30     type wchar_t is implementation-defined;

31     wide_nul : constant wchar_t := wchar_t'First;

32     function To_C   (Item : in Wide_Character) return wchar_t;
       function To_Ada (Item : in wchar_t       ) return Wide_Character;

33     type wchar_array is array (size_t range <>) of aliased wchar_t;

34     pragma Pack(wchar_array);

35     function Is_Nul_Terminated (Item : in wchar_array) return Boolean;

36     function To_C   (Item       : in Wide_String;
                        Append_Nul : in Boolean := True)
          return wchar_array;

37     function To_Ada (Item     : in wchar_array;
                        Trim_Nul : in Boolean := True)
          return Wide_String;

38     procedure To_C (Item       : in  Wide_String;
                       Target     : out wchar_array;
                       Count      : out size_t;
                       Append_Nul : in  Boolean := True);

39     procedure To_Ada (Item     : in  wchar_array;
                         Target   : out Wide_String;
                         Count    : out Natural;
                         Trim_Nul : in  Boolean := True);

40     Terminator_Error : exception;

41  end Interfaces.C;

{94-4697.a} {94-4491.a} {94-4571.a} {94-4737.a} {94-4913.d} {94-4815.a}
{94-4697.a}

42   Each of the types declared in Interfaces.C is C-compatible.

43   The types int, short, long, unsigned, ptrdiff_t, size_t, double, char,
and wchar_t correspond respectively to the C types having the same names.
The types signed_char, unsigned_short, unsigned_long, unsigned_char, C_float,
and long_double correspond respectively to the C types signed char, unsigned
short, unsigned long, unsigned char, float, and long double.

44   The type of the subtype plain_char is either signed_char or unsigned_
char, depending on the C implementation.


45  function To_C   (Item : in Character) return char;
    function To_Ada (Item : in char     ) return Character;

        46   The functions To_C and To_Ada map between the Ada type Character
        and the C type char.


47  function Is_Nul_Terminated (Item : in char_array) return Boolean;

        48   The result of Is_Nul_Terminated is True if Item contains nul,
        and is False otherwise.  {94-4697.a}


49  function To_C   (Item : in String;     Append_Nul : in Boolean := True)
       return char_array;

    function To_Ada (Item : in char_array; Trim_Nul   : in Boolean := True)
       return String;

        50   The result of To_C is a char_array value of length Item'Length
        (if Append_Nul is False) or Item'Length+1 (if Append_Nul is True).
        The lower bound is 0.  For each component Item(I), the corresponding
        component in the result is To_C applied to Item(I).  The value nul is
        appended if Append_Nul is True.
        51   The result of To_Ada is a String whose length is Item'Length (if
        Trim_Nul is False) or the length of the slice of Item preceding the
        first nul (if Trim_Nul is True).  The lower bound of the result is 1.
        If Trim_Nul is False, then for each component Item(I) the
        corresponding component in the result is To_Ada applied to Item(I).
        If Trim_Nul is True, then for each component Item(I) before the first
        nul the corresponding component in the result is To_Ada applied to
        Item(I).  The function propagates Terminator_Error if Trim_Nul is
        True and Item does not contain nul.


52  procedure To_C (Item       : in String;
                    Target     : out char_array;
                    Count      : out size_t;
                    Append_Nul : in Boolean := True);

    procedure To_Ada (Item     : in char_array;
                      Target   : out String;
                      Count    : out Natural;
                      Trim_Nul : in Boolean := True);

        {94-4491.a} {94-4571.a} {94-4737.a} {94-4913.d}
        53   For procedure To_C, each element of Item is converted (via the
        To_C function) to a char, which is assigned to the corresponding
        element of Target.  If Append_Nul is True, nul is then assigned to
        the next element of Target.  In either case, Count is set to the
        number of Target elements assigned.  {Constraint_Error (raised by
        failure of run-time check)} If Target is not long enough, Constraint_
        Error is propagated.
        54   For procedure To_Ada, each element of Item (if Trim_Nul is
        False) or each element of Item preceding the first nul (if Trim_Nul
        is True) is converted (via the To_Ada function) to a Character, which
        is assigned to the corresponding element of Target.  Count is set to
        the number of Target elements assigned.  {Constraint_Error (raised by
        failure of run-time check)} If Target is not long enough, Constraint_
        Error is propagated.  If Trim_Nul is True and Item does not contain
        nul, then Terminator_Error is propagated.


55  function Is_Nul_Terminated (Item : in wchar_array) return Boolean;

        56   The result of Is_Nul_Terminated is True if Item contains wide_
        nul, and is False otherwise.  {94-4697.a}


57  function To_C   (Item : in Wide_Character) return wchar_t;
    function To_Ada (Item : in wchar_t       ) return Wide_Character;

        58   To_C and To_Ada provide the mappings between the Ada and C wide
        character types.


59  function To_C   (Item       : in Wide_String;
                     Append_Nul : in Boolean := True)
       return wchar_array;

    function To_Ada (Item     : in wchar_array;
                     Trim_Nul : in Boolean := True)
       return Wide_String;

    procedure To_C (Item       : in Wide_String;
                    Target     : out wchar_array;
                    Count      : out size_t;
                    Append_Nul : in Boolean := True);

    procedure To_Ada (Item     : in wchar_array;
                      Target   : out Wide_String;
                      Count    : out Natural;
                      Trim_Nul : in Boolean := True);

        {94-4491.a} {94-4571.a} {94-4737.a} {94-4913.d}
        60   The To_C and To_Ada subprograms that convert between Wide_String
        and wchar_array have analogous effects to the To_C and To_Ada
        subprograms that convert between String and char_array, except that
        wide_nul is used instead of nul.

        60.a   Discussion:  The Interfaces.C package provides an
        implementation-defined character type, char, designed to model the C
        run-time character set, and mappings between the types char and
        Character.
        60.b   One application of the C interface package is to compose a C
        string and pass it to a C function.  One way to do this is for the
        programmer to declare an object that will hold the C array, and then
        pass this array to the C function.  This is realized via the type
        char_array:

60.c        type char_array is array (size_t range <>) of Char;

        60.d   The programmer can declare an Ada String, convert it to a
        char_array, and pass the char_array as actual parameter to the C
        function that is expecting a char *.
        60.e   An alternative approach is for the programmer to obtain a C
        char pointer from an Ada String (or from a char_array) by invoking an
        allocation function.  The package Interfaces.C.Strings (see below)
        supplies the needed facilities, including a private type chars_ptr
        that corresponds to C's char *, and two allocation functions.  To
        avoid storage leakage, a Free procedure releases the storage that was
        allocated by one of these allocate functions.
        60.f   It is typical for a C function that deals with strings to
        adopt the convention that the string is delimited by a nul char.  The
        C interface packages support this convention.  A constant nul of type
        Char is declared, and the function Value(Chars_Ptr) in Interfaces.C.-
        Strings returns a char_array up to and including the first nul in the
        array that the chars_ptr points to.  The Allocate_Chars function
        allocates an array that is nul terminated.
        60.g   Some C functions that deal with strings take an explicit
        length as a parameter, thus allowing strings to be passed that
        contain nul as a data element.  Other C functions take an explicit
        length that is an upper bound: the prefix of the string up to the
        char before nul, or the prefix of the given length, is used by the
        function, whichever is shorter.  The C Interface packages support
        calling such functions.


                         Implementation Requirements

61   An implementation shall support pragma Convention with a C
convention_identifier for a C-eligible type (see B.1)


                         Implementation Permissions

62   An implementation may provide additional declarations in the C interface
packages.


{94-4809.b}

                            Implementation Advice

63   An implementation should support the following interface correspondences
between Ada and C.

   64  An Ada procedure corresponds to a void-returning C function.

 64.a   Discussion:  The programmer can also choose an Ada procedure
        when the C function returns an int that is to be discarded.

   65  An Ada function corresponds to a non-void C function.

   66  An Ada in scalar parameter is passed as a scalar argument to a C
       function.

   67  An Ada in parameter of an access-to-object type with designated
       type T is passed as a t* argument to a C function, where t is the
       C type corresponding to the Ada type T.

   68  An Ada access T parameter, or an Ada out or in out parameter of
       an elementary type T, is passed as a t* argument to a C function,
       where t is the C type corresponding to the Ada type T. In the
       case of an elementary out or in out parameter, a pointer to a
       temporary copy is used to preserve by-copy semantics.

 68.a   Change:  Changed ``scalar'' to ``elementary'' in second sentence; the
        by-copy types are elementary, not just scalars.

   69  An Ada parameter of a record type T, of any mode, is passed as a
       t* argument to a C function, where t is the C struct
       corresponding to the Ada type T.

   70  An Ada parameter of an array type with component type T, of any
       mode, is passed as a t* argument to a C function, where t is the
       C type corresponding to the Ada type T.

   71  An Ada parameter of an access-to-subprogram type is passed as a
       pointer to a C function whose prototype corresponds to the
       designated subprogram's specification.


     NOTES
72   (9) Values of type char_array are not implicitly terminated with nul.
     If a char_array is to be passed as a parameter to an imported C function
     requiring nul termination, it is the programmer's responsibility to
     obtain this effect.

73   (10) To obtain the effect of C's sizeof(item_type), where Item_Type is
     the corresponding Ada type, evaluate the expression: size_t(Item_
     Type'Size/CHAR_BIT).

74   (11) There is no explicit support for C's union types.  Unchecked
     conversions can be used to obtain the effect of C unions.

75   (12) A C function that takes a variable number of arguments can
     correspond to several Ada subprograms, taking various specific numbers
     and types of parameters.


                                  Examples

76   Example of using the Interfaces.C package:

77  --Calling the C Library Function strcpy
    with Interfaces.C;
    procedure Test is
       package C renames Interfaces.C;
       use type C.char_array;
       -- Call <string.h>strcpy:
       -- C definition of strcpy:  char *strcpy(char *s1, const char *s2);
       --    This function copies the string pointed to by s2 (including the te\
rminating null character)
       --     into the array pointed to by s1.  If copying takes place between \
objects that overlap,
       --     the behavior is undefined.  The strcpy function returns the value\
 of s1.

78     -- Note: since the C function's return value is of no interest, the Ada \
interface is a procedure
       procedure Strcpy (Target : out C.char_array;
                         Source : in  C.char_array);

79     pragma Import(C, Strcpy, "strcpy");

80     Chars1 :  C.char_array(1..20);
       Chars2 :  C.char_array(1..20);

81  begin
       Chars2(1..6) := "qwert" & C.nul;

82     Strcpy(Chars1, Chars2);

83  -- Now Chars1(1..6) = "qwert" & C.Nul

84  end Test;



B.3.1 The Package Interfaces.C.Strings

1   The package Interfaces.C.Strings declares types and subprograms allowing
an Ada program to allocate, reference, update, and free C-style strings.  In
particular, the private type chars_ptr corresponds to a common use of ``char
*'' in C programs, and an object of this type can be passed to a subprogram
to which pragma Import(C,...) has been applied, and for which ``char *'' is
the type of the argument of the C function.


                              Static Semantics

2   The library package Interfaces.C.Strings has the following declaration:

3   package Interfaces.C.Strings is
       pragma Preelaborate(Strings);

4      type char_array_access is access all char_array;

5      type chars_ptr is private;

6      type chars_ptr_array is array (size_t range <>) of chars_ptr;

7      Null_Ptr : constant chars_ptr;

8      function To_Chars_Ptr (Item      : in char_array_access;
                              Nul_Check : in Boolean := False)
          return chars_ptr;

9      function New_Char_Array (Chars   : in char_array) return chars_ptr;

10     function New_String (Str : in String) return chars_ptr;

11     procedure Free (Item : in out chars_ptr);

12     Dereference_Error : exception;

13     function Value (Item : in chars_ptr) return char_array;

14     function Value (Item : in chars_ptr; Length : in size_t)
          return char_array;

15     function Value (Item : in chars_ptr) return String;

16     function Value (Item : in chars_ptr; Length : in size_t)
          return String;

17     function Strlen (Item : in chars_ptr) return size_t;

18     procedure Update (Item   : in chars_ptr;
                         Offset : in size_t;
                         Chars  : in char_array;
                         Check  : in Boolean := True);

19     procedure Update (Item   : in chars_ptr;
                         Offset : in size_t;
                         Str    : in String;
                         Check  : in Boolean := True);

20     Update_Error : exception;

21  private
       ... -- not specified by the language
    end Interfaces.C.Strings;

{94-4697.a}

        21.a   Discussion:  The string manipulation types and subprograms
        appear in a child of Interfaces.C versus being there directly, since
        it is useful to have Interfaces.C specified as pragma Pure.

        21.b   Differently named functions New_String and New_Char_Array are
        declared, since if there were a single overloaded function a call
        with a string literal as actual parameter would be ambiguous.

22   The type chars_ptr is C-compatible and corresponds to the use of C's
``char *'' for a pointer to the first char in a char array terminated by nul.
When an object of type chars_ptr is declared, its value is by default set to
Null_Ptr, unless the object is imported (see B.1).

        22.a   Discussion:  The type char_array_access is not necessarily
        C-compatible, since an object of this type may carry ``dope''
        information.  The programmer should convert from char_array_access to
        chars_ptr for objects imported from, exported to, or passed to C.


23  function To_Chars_Ptr (Item      : in char_array_access;
                           Nul_Check : in Boolean := False)
       return chars_ptr;
        {94-4697.a}
        24   If Item is null, then To_Chars_Ptr returns Null_Ptr.  Otherwise,
        if Nul_Check is True and Item.all does not contain nul, then the
        function propagates Terminator_Error; if Nul_Check is True and
        Item.all does contain nul, To_Chars_Ptr performs a pointer conversion
        with no allocation of memory.


25  function New_Char_Array (Chars   : in char_array) return chars_ptr;

        26   This function returns a pointer to an allocated object
        initialized to Chars(Chars'First .. Index) & nul, where

           27  Index = Chars'Last if Chars does not contain nul, or

           28  Index is the smallest size_t value I such that Chars(I+1)
               = nul.

        Storage_Error is propagated if the allocation fails.  {94-4805.b}
        {94-4807.b}


29  function New_String (Str : in String) return chars_ptr;

        30   This function is equivalent to New_Char_Array(To_C(Str)).


31  procedure Free (Item : in out chars_ptr);

        32   If Item is Null_Ptr, then Free has no effect.  Otherwise, Free
        releases the storage occupied by Value(Item), and resets Item to
        Null_Ptr.


33  function Value (Item : in chars_ptr) return char_array;

        34   If Item = Null_Ptr then Value propagates Dereference_Error.
        Otherwise Value returns the prefix of the array of chars pointed to
        by Item, up to and including the first nul.  The lower bound of the
        result is 0.  If Item does not point to a nul-terminated string, then
        execution of Value is erroneous.


35  function Value (Item : in chars_ptr; Length : in size_t)
       return char_array;

        36   If Item = Null_Ptr then Value(Item) propagates Dereference_
        Error.  Otherwise Value returns the shorter of two arrays:  the first
        Length chars pointed to by Item, and Value(Item).  The lower bound of
        the result is 0.

        36.a   Ramification:  Value(New_Char_Array(Chars)) = Chars if Chars
        does not contain nul; else Value(New_Char_Array(Chars)) is the prefix
        of Chars up to and including the first nul.


37  function Value (Item : in chars_ptr) return String;

        38   Equivalent to To_Ada(Value(Item), Trim_Nul=>True).


39  function Value (Item : in chars_ptr; Length : in size_t)
       return String;

        40   Equivalent to To_Ada(Value(Item, Length), Trim_Nul=>True).


41  function Strlen (Item : in chars_ptr) return size_t;

        42   Returns Val'Length-1 where Val = Value(Item); propagates
        Dereference_Error if Item = Null_Ptr.

        42.a   Ramification:  Strlen returns the number of chars in the array
        pointed to by Item, up to and including the char immediately before
        the first nul.
        42.b   Strlen has the same possibility for erroneous execution as
        Value, in cases where the string has not been nul-terminated.
        42.c   Strlen has the effect of C's strlen function.


43  procedure Update (Item   : in chars_ptr;
                      Offset : in size_t;
                      Chars  : in char_array;
                      Check  : Boolean := True);

        44   This procedure updates the value pointed to by Item, starting at
        position Offset, using Chars as the data to be copied into the array.
        Overwriting the nul terminator, and skipping with the Offset past the
        nul terminator, are both prevented if Check is True, as follows:

           45  Let N = Strlen(Item).  If Check is True, then:

                  46  If Offset+Chars'Length>N, propagate Update_Error.

                  47  Otherwise, overwrite the data in the array pointed
                      to by Item, starting at the char at position
                      Offset, with the data in Chars.

           48  If Check is False, then processing is as above, but with
               no check that Offset+Chars'Length>N.

 48.a   Ramification:  If Chars contains nul, Update's effect may be to
        ``shorten'' the pointed-to char array.


49  procedure Update (Item   : in chars_ptr;
                      Offset : in size_t;
                      Str    : in String;
                      Check  : in Boolean := True);

        50   Equivalent to Update(Item, Offset, To_C(Str), Check).


                             Erroneous Execution

51   {erroneous execution} Execution of any of the following is erroneous if
the Item parameter is not null_ptr and Item does not point to a
nul-terminated array of chars.

   52  a Value function not taking a Length parameter,

   53  the Free procedure,

   54  the Strlen function.

55   Execution of Free(X) is also erroneous if the chars_ptr X was not
returned by New_Char_Array or New_String.

56   Reading or updating a freed char_array is erroneous.

57   Execution of Update is erroneous if Check is False and a call with Check
equal to True would have propagated Update_Error.


     NOTES
58   (13) New_Char_Array and New_String might be implemented either through
     the allocation function from the C environment (``malloc'') or through
     Ada dynamic memory allocation (``new''). The key points are

        59  the returned value (a chars_ptr) is represented as a C
            ``char *'' so that it may be passed to C functions;

        60  the allocated object should be freed by the programmer via a
            call of Free, not by a called C function.



B.3.2 The Generic Package Interfaces.C.Pointers

1   The generic package Interfaces.C.Pointers allows the Ada programmer to
perform C-style operations on pointers.  It includes an access type Pointer,
Value functions that dereference a Pointer and deliver the designated array,
several pointer arithmetic operations, and ``copy'' procedures that copy the
contents of a source pointer into the array designated by a destination
pointer.  As in C, it treats an object Ptr of type Pointer as a pointer to
the first element of an array, so that for example, adding 1 to Ptr yields a
pointer to the second element of the array.

2   The generic allows two styles of usage: one in which the array is
terminated by a special terminator element; and another in which the
programmer needs to keep track of the length.


                              Static Semantics

3   The generic library package Interfaces.C.Pointers has the following
declaration:

4   generic
       type Index is (<>);
       type Element is private;
       type Element_Array is array (Index range <>) of aliased Element;
       Default_Terminator : Element;
    package Interfaces.C.Pointers is
       pragma Preelaborate(Pointers);

5      type Pointer is access all Element;

6      function Value(Ref        : in Pointer;
                      Terminator : in Element := Default_Terminator)
          return Element_Array;

7      function Value(Ref    : in Pointer;
                      Length : in ptrdiff_t)
          return Element_Array;

8      Pointer_Error : exception;

9      -- C-style Pointer arithmetic

10     function "+" (Left : in Pointer;   Right : in ptrdiff_t) return Pointer;
       function "+" (Left : in ptrdiff_t; Right : in Pointer)   return Pointer;
       function "-" (Left : in Pointer;   Right : in ptrdiff_t) return Pointer;
       function "-" (Left : in Pointer;   Right : in Pointer)   return ptrdiff_\
t;

11     procedure Increment (Ref : in out Pointer);
       procedure Decrement (Ref : in out Pointer);

12     pragma Convention (Intrinsic, "+");
       pragma Convention (Intrinsic, "-");
       pragma Convention (Intrinsic, Increment);
       pragma Convention (Intrinsic, Decrement);

13     function Virtual_Length (Ref        : in Pointer;
                                Terminator : in Element := Default_Terminator)
          return ptrdiff_t;

14     procedure Copy_Terminated_Array (Source     : in Pointer;
                                        Target     : in Pointer;
                                        Limit      : in ptrdiff_t := ptrdiff_t'\
Last;
                                        Terminator : in Element :=  Default_Ter\
minator);

15     procedure Copy_Array (Source  : in Pointer;
                             Target  : in Pointer;
                             Length  : in ptrdiff_t);

16  end Interfaces.C.Pointers;

{94-4981.a}

17   The type Pointer is C-compatible and corresponds to one use of C's
``Element *''.  An object of type Pointer is interpreted as a pointer to the
initial Element in an Element_Array.  Two styles are supported:

   18  Explicit termination of an array value with Default_Terminator (a
       special terminator value);

   19  Programmer-managed length, with Default_Terminator treated simply
       as a data element.


20  function Value(Ref        : in Pointer;
                   Terminator : in Element := Default_Terminator)
       return Element_Array;

        21   This function returns an Element_Array whose value is the array
        pointed to by Ref, up to and including the first Terminator; the
        lower bound of the array is Index'First.  Interfaces.C.Strings.-
        Dereference_Error is propagated if Ref is null.


22  function Value(Ref    : in Pointer;
                   Length : in ptrdiff_t)
       return Element_Array;

        23   This function returns an Element_Array comprising the first
        Length elements pointed to by Ref.  The exception Interfaces.C.-
        Strings.Dereference_Error is propagated if Ref is null.  {94-4965.a}

24   The "+" and "-" functions perform arithmetic on Pointer values, based on
the Size of the array elements.  In each of these functions, Pointer_Error is
propagated if a Pointer parameter is null.


25  procedure Increment (Ref : in out Pointer);

        26   Equivalent to Ref := Ref+1.


27  procedure Decrement (Ref : in out Pointer);

        28   Equivalent to Ref := Ref-1.


29  function Virtual_Length (Ref        : in Pointer;
                             Terminator : in Element := Default_Terminator)
       return ptrdiff_t;

        30   Returns the number of Elements, up to the one just before the
        first Terminator, in Value(Ref, Terminator).


31  procedure Copy_Terminated_Array (Source     : in Pointer;
                                     Target     : in Pointer;
                                     Limit      : in ptrdiff_t := ptrdiff_t'Las\
t;
                                     Terminator : in Element := Default_Termina\
tor);

        32   This procedure copies Value(Source, Terminator) into the array
        pointed to by Target; it stops either after Terminator has been
        copied, or the number of elements copied is Limit, whichever occurs
        first.  Dereference_Error is propagated if either Source or Target is
        null.

        32.a   Ramification:  It is the programmer's responsibility to ensure
        that elements are not copied beyond the logical length of the target
        array.

        32.b   Implementation Note:  The implementation has to take care to
        check the Limit first.


33  procedure Copy_Array (Source  : in Pointer;
                          Target  : in Pointer;
                          Length  : in ptrdiff_t);

        34   This procedure copies the first Length elements from the array
        pointed to by Source, into the array pointed to by Target.
        Dereference_Error is propagated if either Source or Target is null.


                             Erroneous Execution

35   {erroneous execution} It is erroneous to dereference a Pointer that does
not designate an aliased Element.

        35.a   Discussion:  Such a Pointer could arise via "+", "-",
        Increment, or Decrement.

36   Execution of Value(Ref, Terminator) is erroneous if Ref does not
designate an aliased Element in an Element_Array terminated by Terminator.

37   Execution of Value(Ref, Length) is erroneous if Ref does not designate
an aliased Element in an Element_Array containing at least Length Elements
between the designated Element and the end of the array, inclusive.

38   Execution of Virtual_Length(Ref, Terminator) is erroneous if Ref does
not designate an aliased Element in an Element_Array terminated by
Terminator.

39   Execution of Copy_Terminated_Array(Source, Target, Limit, Terminator) is
erroneous in either of the following situations:

   40  Execution of both Value(Source,Terminator) and
       Value(Source,Limit) are erroneous, or

   41  Copying writes past the end of the array containing the Element
       designated by Target.

42   Execution of Copy_Array(Source, Target, Length) is erroneous if either
Value(Source, Length) is erroneous, or copying writes past the end of the
array containing the Element designated by Target.


     NOTES
43   (14) To compose a Pointer from an Element_Array, use 'Access on the
     first element.  For example (assuming appropriate instantiations):

44       Some_Array   : Element_Array(0..5) ;
         Some_Pointer : Pointer := Some_Array(0)'Access;


                                  Examples

45   Example of Interfaces.C.Pointers:

46  with Interfaces.C.Pointers;
    with Interfaces.C.Strings;
    procedure Test_Pointers is
       package C renames Interfaces.C;
       package Char_Ptrs is
          new C.Pointers (Index              => C.size_t,
                          Element            => C.char,
                          Element_Array      => C.char_array,
                          Default_Terminator => C.nul);

47     use type Char_Ptrs.Pointer;
       subtype Char_Star is Char_Ptrs.Pointer;

48     procedure Strcpy (Target_Ptr, Source_Ptr : Char_Star) is
          Target_Temp_Ptr : Char_Star := Target_Ptr;
          Source_Temp_Ptr : Char_Star := Source_Ptr;
          Element : C.char;
       begin
          if Target_Temp_Ptr = null or Source_Temp_Ptr = null then
             raise C.Strings.Dereference_Error;
          end if;

49        loop
             Element             := Source_Temp_Ptr.all;
             Target_Temp_Ptr.all := Element;
             exit when Element = C.nul;
             Char_Ptrs.Increment(Target_Temp_Ptr);
             Char_Ptrs.Increment(Source_Temp_Ptr);
          end loop;
       end Strcpy;
    begin
       ...
    end Test_Pointers;



B.4 Interfacing with COBOL

1   {interface to COBOL} {COBOL interface} The facilities relevant to
interfacing with the COBOL language are the package Interfaces.COBOL and
support for the Import, Export and Convention pragmas with
convention_identifier COBOL.

2   The COBOL interface package supplies several sets of facilities:

    3  A set of types corresponding to the native COBOL types of the
       supported COBOL implementation (so-called ``internal COBOL
       representations''), allowing Ada data to be passed as parameters
       to COBOL programs

    4  A set of types and constants reflecting external data
       representations such as might be found in files or databases,
       allowing COBOL-generated data to be read by an Ada program, and
       Ada-generated data to be read by COBOL programs

    5  A generic package for converting between an Ada decimal type
       value and either an internal or external COBOL representation


                              Static Semantics

6   The library package Interfaces.COBOL has the following declaration:

7   package Interfaces.COBOL is
       pragma Preelaborate(COBOL);

8   -- Types and operations for internal data representations

9      type Floating      is digits implementation-defined;
       type Long_Floating is digits implementation-defined;

10     type Binary      is range implementation-defined;
       type Long_Binary is range implementation-defined;

11     Max_Digits_Binary      : constant := implementation-defined;
       Max_Digits_Long_Binary : constant := implementation-defined;

12     type Decimal_Element  is mod implementation-defined;
       type Packed_Decimal is array (Positive range <>) of Decimal_Element;
       pragma Pack(Packed_Decimal);

13     type COBOL_Character is implementation-defined character type;

14     Ada_To_COBOL : array (Character) of COBOL_Character := implementation-de\
fined;

15     COBOL_To_Ada : array (COBOL_Character) of Character := implementation-de\
fined;

16     type Alphanumeric is array (Positive range <>) of COBOL_Character;
       pragma Pack(Alphanumeric);

17     function To_COBOL (Item : in String) return Alphanumeric;
       function To_Ada   (Item : in Alphanumeric) return String;

18     procedure To_COBOL (Item       : in String;
                           Target     : out Alphanumeric;
                           Last       : out Natural);

19     procedure To_Ada (Item     : in Alphanumeric;
                         Target   : out String;
                         Last     : out Natural);

20     type Numeric is array (Positive range <>) of COBOL_Character;
       pragma Pack(Numeric);

21  -- Formats for COBOL data representations

22     type Display_Format is private;

23     Unsigned             : constant Display_Format;
       Leading_Separate     : constant Display_Format;
       Trailing_Separate    : constant Display_Format;
       Leading_Nonseparate  : constant Display_Format;
       Trailing_Nonseparate : constant Display_Format;

24     type Binary_Format is private;

25     High_Order_First  : constant Binary_Format;
       Low_Order_First   : constant Binary_Format;
       Native_Binary     : constant Binary_Format;

26     type Packed_Format is private;

27     Packed_Unsigned   : constant Packed_Format;
       Packed_Signed     : constant Packed_Format;

28  -- Types for external representation of COBOL binary data

29     type Byte is mod 2**COBOL_Character'Size;
       type Byte_Array is array (Positive range <>) of Byte;
       pragma Pack (Byte_Array);

30     Conversion_Error : exception;

31     generic
          type Num is delta <> digits <>;
       package Decimal_Conversions is

32        -- Display Formats: data values are represented as Numeric

33        function Valid (Item   : in Numeric;
                          Format : in Display_Format) return Boolean;

34        function Length (Format : in Display_Format) return Natural;

35        function To_Decimal (Item   : in Numeric;
                               Format : in Display_Format) return Num;

36        function To_Display (Item   : in Num;
                               Format : in Display_Format) return Numeric;

37        -- Packed Formats: data values are represented as Packed_Decimal

38        function Valid (Item   : in Packed_Decimal;
                          Format : in Packed_Format) return Boolean;

39        function Length (Format : in Packed_Format) return Natural;

40        function To_Decimal (Item   : in Packed_Decimal;
                               Format : in Packed_Format) return Num;

41        function To_Packed (Item   : in Num;
                              Format : in Packed_Format) return Packed_Decimal;

42        -- Binary Formats: external data values are represented as Byte_Array

43        function Valid (Item   : in Byte_Array;
                          Format : in Binary_Format) return Boolean;

44        function Length (Format : in Binary_Format) return Natural;
          function To_Decimal (Item   : in Byte_Array;
                               Format : in Binary_Format) return Num;

45        function To_Binary (Item   : in Num;
                            Format : in Binary_Format) return Byte_Array;

46        -- Internal Binary formats: data values are of type Binary or Long_Bi\
nary

47        function To_Decimal (Item : in Binary)      return Num;
          function To_Decimal (Item : in Long_Binary) return Num;

48        function To_Binary      (Item : in Num)  return Binary;
          function To_Long_Binary (Item : in Num)  return Long_Binary;

49     end Decimal_Conversions;

50  private
       ... -- not specified by the language
    end Interfaces.COBOL;

{94-4980.a}

        50.a   Implementation defined:  The types Floating, Long_Floating,
        Binary, Long_Binary, Decimal_Element, and COBOL_Character; and the
        initializations of the variables Ada_To_COBOL and COBOL_To_Ada, in
        Interfaces.COBOL

51   Each of the types in Interfaces.COBOL is COBOL-compatible.

52   The types Floating and Long_Floating correspond to the native types in
COBOL for data items with computational usage implemented by floating point.
The types Binary and Long_Binary correspond to the native types in COBOL for
data items with binary usage, or with computational usage implemented by
binary.

53   Max_Digits_Binary is the largest number of decimal digits in a numeric
value that is represented as Binary.  Max_Digits_Long_Binary is the largest
number of decimal digits in a numeric value that is represented as Long_
Binary.

54   The type Packed_Decimal corresponds to COBOL's packed-decimal usage.

55   The type COBOL_Character defines the run-time character set used in the
COBOL implementation.  Ada_To_COBOL and COBOL_To_Ada are the mappings between
the Ada and COBOL run-time character sets.

        55.a   Reason:  The character mappings are visible variables, since
        the user needs the ability to modify them at run time.

56   Type Alphanumeric corresponds to COBOL's alphanumeric data category.

57   Each of the functions To_COBOL and To_Ada converts its parameter based
on the mappings Ada_To_COBOL and COBOL_To_Ada, respectively.  The length of
the result for each is the length of the parameter, and the lower bound of
the result is 1.  Each component of the result is obtained by applying the
relevant mapping to the corresponding component of the parameter.

58   Each of the procedures To_COBOL and To_Ada copies converted elements
from Item to Target, using the appropriate mapping (Ada_To_COBOL or COBOL_To_
Ada, respectively).  The index in Target of the last element assigned is
returned in Last (0 if Item is a null array).  {Constraint_Error (raised by
failure of run-time check)} If Item'Length exceeds Target'Length, Constraint_
Error is propagated.

59   Type Numeric corresponds to COBOL's numeric data category with display
usage.

60   The types Display_Format, Binary_Format, and Packed_Format are used in
conversions between Ada decimal type values and COBOL internal or external
data representations.  The value of the constant Native_Binary is either
High_Order_First or Low_Order_First, depending on the implementation.


61  function Valid (Item   : in Numeric;
                    Format : in Display_Format) return Boolean;

        62   The function Valid checks that the Item parameter has a value
        consistent with the value of Format.  If the value of Format is other
        than Unsigned, Leading_Separate, and Trailing_Separate, the effect is
        implementation defined.  If Format does have one of these values, the
        following rules apply:

           63  Format=Unsigned: if Item comprises zero or more leading
               space characters followed by one or more decimal digit
               characters then Valid returns True, else it returns
               False.

           64  Format=Leading_Separate: if Item comprises zero or more
               leading space characters, followed by a single occurrence
               of the plus or minus sign character, and then one or more
               decimal digit characters, then Valid returns True, else
               it returns False.

           65  Format=Trailing_Separate: if Item comprises zero or more
               leading space characters, followed by one or more decimal
               digit characters and finally a plus or minus sign
               character, then Valid returns True, else it returns
               False.


66  function Length (Format : in Display_Format) return Natural;

        67   The Length function returns the minimal length of a Numeric
        value sufficient to hold any value of type Num when represented as
        Format.


68  function To_Decimal (Item   : in Numeric;
                         Format : in Display_Format) return Num;

        69   Produces a value of type Num corresponding to Item as
        represented by Format.  The number of digits after the assumed radix
        point in Item is Num'Scale.  Conversion_Error is propagated if the
        value represented by Item is outside the range of Num.

        69.a   Discussion:  There is no issue of truncation versus rounding,
        since the number of decimal places is established by Num'Scale.


70  function To_Display (Item   : in Num;
                         Format : in Display_Format) return Numeric;

        71   This function returns the Numeric value for Item, represented in
        accordance with Format.  Conversion_Error is propagated if Num is
        negative and Format is Unsigned.


72  function Valid (Item   : in Packed_Decimal;
                    Format : in Packed_Format) return Boolean;

        {94-4980.a}
        73   This function returns True if Item has a value consistent with
        Format, and False otherwise.  The rules for the formation of Packed_
        Decimal values are implementation defined.


74  function Length (Format : in Packed_Format) return Natural;

        75   This function returns the minimal length of a Packed_Decimal
        value sufficient to hold any value of type Num when represented as
        Format.


76  function To_Decimal (Item   : in Packed_Decimal;
                         Format : in Packed_Format) return Num;

        77   Produces a value of type Num corresponding to Item as
        represented by Format.  Num'Scale is the number of digits after the
        assumed radix point in Item.  Conversion_Error is propagated if the
        value represented by Item is outside the range of Num.


78  function To_Packed (Item   : in Num;
                        Format : in Packed_Format) return Packed_Decimal;

        79   This function returns the Packed_Decimal value for Item,
        represented in accordance with Format.  Conversion_Error is
        propagated if Num is negative and Format is Packed_Unsigned.


80  function Valid (Item   : in Byte_Array;
                    Format : in Binary_Format) return Boolean;

        81   This function returns True if Item has a value consistent with
        Format, and False otherwise.

        81.a   Ramification:  This function returns False only when the
        represented value is outside the range of Num.


82  function Length (Format : in Binary_Format) return Natural;

        83   This function returns the minimal length of a Byte_Array value
        sufficient to hold any value of type Num when represented as Format.


84  function To_Decimal (Item   : in Byte_Array;
                         Format : in Binary_Format) return Num;

        85   Produces a value of type Num corresponding to Item as
        represented by Format.  Num'Scale is the number of digits after the
        assumed radix point in Item.  Conversion_Error is propagated if the
        value represented by Item is outside the range of Num.


86  function To_Binary (Item   : in Num;
                        Format : in Binary_Format) return Byte_Array;

        87   This function returns the Byte_Array value for Item, represented
        in accordance with Format.


88  function To_Decimal (Item : in Binary)      return Num;

    function To_Decimal (Item : in Long_Binary) return Num;

        89   These functions convert from COBOL binary format to a
        corresponding value of the decimal type Num.  Conversion_Error is
        propagated if Item is too large for Num.

        89.a   Ramification:  There is no rescaling performed on the
        conversion.  That is, the returned value in each case is a ``bit
        copy'' if Num has a binary radix.  The programmer is responsible for
        maintaining the correct scale.


90  function To_Binary      (Item : in Num)  return Binary;

    function To_Long_Binary (Item : in Num)  return Long_Binary;

        91   These functions convert from Ada decimal to COBOL binary format.
        Conversion_Error is propagated if the value of Item is too large to
        be represented in the result type.

        91.a   Discussion:  One style of interface supported for COBOL,
        similar to what is provided for C, is the ability to call and pass
        parameters to an existing COBOL program.  Thus the interface package
        supplies types that can be used in an Ada program as parameters to
        subprograms whose bodies will be in COBOL.  These types map to
        COBOL's alphanumeric and numeric data categories.
        91.b   Several types are provided for support of alphanumeric data.
        Since COBOL's run-time character set is not necessarily the same as
        Ada's, Interfaces.COBOL declares an implementation-defined character
        type COBOL_Character, and mappings between Character and COBOL_
        Character.  These mappings are visible variables (rather than, say,
        functions or constant arrays), since in the situation where COBOL_
        Character is EBCDIC, the flexibility of dynamically modifying the
        mappings is needed.  Corresponding to COBOL's alphanumeric data is
        the string type Alphanumeric.
        91.c   Numeric data may have either a ``display'' or ``computa-
        tional'' representation in COBOL.  On the Ada side, the data is of a
        decimal fixed point type.  Passing an Ada decimal data item to a
        COBOL program requires conversion from the Ada decimal type to some
        type that reflects the representation expected on the COBOL side.

         91.d  Computational Representation

               91.e   Floating point representation is modeled by Ada
               floating point types, Floating and Long_Floating.
               Conversion between these types and Ada decimal types is
               obtained directly, since the type name serves as a
               conversion function.

               91.f   Binary representation is modeled by an Ada integer
               type, Binary, and possibly other types such as Long_
               Binary.  Conversion between, say, Binary and a decimal
               type is through functions from an instantiation of the
               generic package Decimal_Conversions.

               91.g   Packed decimal representation is modeled by the
               Ada array type Packed_Decimal.  Conversion between packed
               decimal and a decimal type is through functions from an
               instantiation of the generic package Decimal_Conversions.

         91.h  Display Representation

               91.i   Display representation for numeric data is modeled
               by the array type Numeric.  Conversion between display
               representation and a decimal type is through functions
               from an instantiation of the generic package Decimal_
               Conversions.  A parameter to the conversion function
               indicates the desired interpretation of the data (e.g.,
               signed leading separate, etc.)

        91.j   Pragma Convention(COBOL, T) may be applied to a record type T
        to direct the compiler to choose a COBOL-compatible representation
        for objects of the type.
        91.k   The package Interfaces.COBOL allows the Ada programmer to deal
        with data from files (or databases) created by a COBOL program.  For
        data that is alphanumeric, or in display or packed decimal format,
        the approach is the same as for passing parameters (instantiate
        Decimal_Conversions to obtain the needed conversion functions).  For
        binary data, the external representation is treated as a Byte array,
        and an instantiation of Decimal_IO produces a package that declares
        the needed conversion functions.  A parameter to the conversion
        function indicates the desired interpretation of the data (e.g.,
        high- versus low-order byte first).


                         Implementation Requirements

92   An implementation shall support pragma Convention with a COBOL
convention_identifier for a COBOL-eligible type (see B.1).
        92.a   Ramification:  An implementation supporting this package shall
        ensure that if the bounds of a Packed_Decimal, Alphanumeric, or
        Numeric variable are static, then the representation of the object
        comprises solely the array components (that is, there is no implicit
        run-time ``descriptor'' that is part of the object).


                         Implementation Permissions

93   An implementation may provide additional constants of the private types
Display_Format, Binary_Format, or Packed_Format.

        93.a   Reason:  This is to allow exploitation of other external
        formats that may be available in the COBOL implementation.

94   An implementation may provide further floating point and integer types
in Interfaces.COBOL to match additional native COBOL types, and may also
supply corresponding conversion functions in the generic package Decimal_
Conversions.


                            Implementation Advice

95   An Ada implementation should support the following interface
correspondences between Ada and COBOL.

   96  An Ada access T parameter is passed as a ``BY REFERENCE'' data
       item of the COBOL type corresponding to T.

   97  An Ada in scalar parameter is passed as a ``BY CONTENT'' data
       item of the corresponding COBOL type.

   98  Any other Ada parameter is passed as a ``BY REFERENCE'' data item
       of the COBOL type corresponding to the Ada parameter type; for
       scalars, a local copy is used if necessary to ensure by-copy
       semantics.


     NOTES
99   (15) An implementation is not required to support pragma Convention for
     access types, nor is it required to support pragma Import, Export or
     Convention for functions.

   99.a   Reason:  COBOL does not have a pointer facility, and a COBOL
        program does not return a value.

100  (16) If an Ada subprogram is exported to COBOL, then a call from COBOL
     call may specify either ``BY CONTENT'' or ``BY REFERENCE''.


                                  Examples

101   Examples of Interfaces.COBOL:

102 with Interfaces.COBOL;
    procedure Test_Call is

103    -- Calling a foreign COBOL program
       -- Assume that a COBOL program PROG has the following declaration
       --  in its LINKAGE section:
       --  01 Parameter-Area
       --     05 NAME   PIC X(20).
       --     05 SSN    PIC X(9).
       --     05 SALARY PIC 99999V99 USAGE COMP.
       -- The effect of PROG is to update SALARY based on some algorithm

104    package COBOL renames Interfaces.COBOL;

105    type Salary_Type is delta 0.01 digits 7;

106    type COBOL_Record is
          record
             Name   : COBOL.Numeric(1..20);
             SSN    : COBOL.Numeric(1..9);
             Salary : COBOL.Binary;  -- Assume Binary = 32 bits
          end record;
       pragma Convention (COBOL, COBOL_Record);

107    procedure Prog (Item : in out COBOL_Record);
       pragma Import (COBOL, Prog, "PROG");

108    package Salary_Conversions is
          new COBOL.Decimal_Conversions(Salary_Type);

109    Some_Salary : Salary_Type := 12_345.67;
       Some_Record : COBOL_Record :=
          (Name   => "Johnson, John       ",
           SSN    => "111223333",
           Salary => Salary_Conversions.To_Binary(Some_Salary));

110 begin
       Prog (Some_Record);
       ...
    end Test_Call;

111 with Interfaces.COBOL;
    with COBOL_Sequential_IO; -- Assumed to be supplied by implementation
    procedure Test_External_Formats is

112    -- Using data created by a COBOL program
       -- Assume that a COBOL program has created a sequential file with
       --  the following record structure, and that we need to
       --  process the records in an Ada program
       --  01 EMPLOYEE-RECORD
       --     05 NAME    PIC X(20).
       --     05 SSN     PIC X(9).
       --     05 SALARY  PIC 99999V99 USAGE COMP.
       --     05 ADJUST  PIC S999V999 SIGN LEADING SEPARATE.
       -- The COMP data is binary (32 bits), high-order byte first

113    package COBOL renames Interfaces.COBOL;

114    type Salary_Type      is delta 0.01  digits 7;
       type Adjustments_Type is delta 0.001 digits 6;

115    type COBOL_Employee_Record_Type is  -- External representation
          record
             Name    : COBOL.Alphanumeric(1..20);
             SSN     : COBOL.Alphanumeric(1..9);
             Salary  : COBOL.Byte_Array(1..4);
             Adjust  : COBOL.Numeric(1..7);  -- Sign and 6 digits
          end record;
       pragma Convention (COBOL, COBOL_Employee_Record_Type);

116    package COBOL_Employee_IO is
          new COBOL_Sequential_IO(COBOL_Employee_Record_Type);
       use COBOL_Employee_IO;

117    COBOL_File : File_Type;

118    type Ada_Employee_Record_Type is  -- Internal representation
          record
             Name    : String(1..20);
             SSN     : String(1..9);
             Salary  : Salary_Type;
             Adjust  : Adjustments_Type;
          end record;

119    COBOL_Record : COBOL_Employee_Record_Type;
       Ada_Record   : Ada_Employee_Record_Type;

120    package Salary_Conversions is
          new COBOL.Decimal_Conversions(Salary_Type);
       use Salary_Conversions;

121    package Adjustments_Conversions is
          new COBOL.Decimal_Conversions(Adjustments_Type);
       use Adjustments_Conversions;

122 begin
       Open (COBOL_File, Name => "Some_File");

123    loop
         Read (COBOL_File, COBOL_Record);

124      Ada_Record.Name := To_Ada(COBOL_Record.Name);
         Ada_Record.SSN  := To_Ada(COBOL_Record.SSN);
         Ada_Record.Salary :=
            To_Decimal(COBOL_Record.Salary, COBOL.High_Order_First);
         Ada_Record.Adjust :=
            To_Decimal(COBOL_Record.Adjust, COBOL.Leading_Separate);
         ... -- Process Ada_Record
       end loop;
    exception
       when End_Error => ...
    end Test_External_Formats;



B.5 Interfacing with Fortran

1   {interface to Fortran} {Fortran interface} The facilities relevant to
interfacing with the Fortran language are the package Interfaces.Fortran and
support for the Import, Export and Convention pragmas with
convention_identifier Fortran.

2   The package Interfaces.Fortran defines Ada types whose representations
are identical to the default representations of the Fortran intrinsic types
Integer, Real, Double Precision, Complex, Logical, and Character in a
supported Fortran implementation.  These Ada types can therefore be used to
pass objects between Ada and Fortran programs.


                              Static Semantics

3   The library package Interfaces.Fortran has the following declaration:

4   with Ada.Numerics.Generic_Complex_Types;  -- see G.1.1
    pragma Elaborate_All(Ada.Numerics.Generic_Complex_Types);
    package Interfaces.Fortran is
       pragma Pure(Fortran);

5      type Fortran_Integer is range implementation-defined;

6      type Real             is digits implementation-defined;
       type Double_Precision is digits implementation-defined;

7      type Logical is new Boolean;

8      package Single_Precision_Complex_Types is
          new Ada.Numerics.Generic_Complex_Types (Real);

9      type Complex is new Single_Precision_Complex_Types.Complex;

10  subtype Imaginary is Single_Precision_Complex_Types.Imaginary;
       i : Imaginary renames Single_Precision_Complex_Types.i;
       j : Imaginary renames Single_Precision_Complex_Types.j;

11

       type Character_Set is implementation-defined character type;

12     type Fortran_Character is array (Positive range <>) of Character_Set;
       pragma Pack (Fortran_Character);

13  function To_Fortran (Item : in Character) return Character_Set;
       function To_Ada (Item : in Character_Set) return Character;

14     function To_Fortran (Item : in String) return Fortran_Character;
       function To_Ada     (Item : in Fortran_Character) return String;

15     procedure To_Fortran (Item       : in String;
                             Target     : out Fortran_Character;
                             Last       : out Natural);

16     procedure To_Ada (Item     : in Fortran_Character;
                         Target   : out String;
                         Last     : out Natural);

17  end Interfaces.Fortran;

        17.a   Ramification:  The means by which the Complex type is provided
        in Interfaces.Fortran creates a dependence of Interfaces.Fortran on
        Numerics.Generic_Complex_Types (see G.1.1).  This dependence is
        intentional and unavoidable, if the Fortran-compatible Complex type
        is to be useful in Ada code without duplicating facilities defined
        elsewhere.

18   The types Fortran_Integer, Real, Double_Precision, Logical, Complex, and
Fortran_Character are Fortran-compatible.

19   The To_Fortran and To_Ada functions map between the Ada type Character
and the Fortran type Character_Set, and also between the Ada type String and
the Fortran type Fortran_Character.  The To_Fortran and To_Ada procedures
have analogous effects to the string conversion subprograms found in
Interfaces.COBOL.


                         Implementation Requirements

20   An implementation shall support pragma Convention with a Fortran
convention_identifier for a Fortran-eligible type (see B.1).


                         Implementation Permissions

21   An implementation may add additional declarations to the Fortran
interface packages.  For example, the Fortran interface package for an
implementation of Fortran 77 (ANSI X3.9-1978) that defines types like
Integer*n, Real*n, Logical*n, and Complex*n may contain the declarations of
types named Integer_Star_n, Real_Star_n, Logical_Star_n, and Complex_Star_n.
(This convention should not apply to Character*n, for which the Ada analog is
the constrained array subtype Fortran_Character (1..n).)  Similarly, the
Fortran interface package for an implementation of Fortran 90 that provides
multiple kinds of intrinsic types, e.g. Integer (Kind=n), Real (Kind=n),
Logical (Kind=n), Complex (Kind=n), and Character (Kind=n), may contain the
declarations of types with the recommended names Integer_Kind_n, Real_Kind_n,
Logical_Kind_n, Complex_Kind_n, and Character_Kind_n.

        21.a   Discussion:  Implementations may add auxiliary declarations as
        needed to assist in the declarations of additional Fortran-compatible
        types.  For example, if a double precision complex type is defined,
        then Numerics.Generic_Complex_Types may be instantiated for the
        double precision type.  Similarly, if a wide character type is
        defined to match a Fortran 90 wide character type (accessible in
        Fortran 90 with the Kind modifier), then an auxiliary character set
        may be declared to serve as its component type.


                            Implementation Advice

22   An Ada implementation should support the following interface
correspondences between Ada and Fortran:

   23  An Ada procedure corresponds to a Fortran subroutine.

   24  An Ada function corresponds to a Fortran function.

   25  An Ada parameter of an elementary, array, or record type T is
       passed as a T  argument to a Fortran procedure, where T  is the
                    F                                         F
       Fortran type corresponding to the Ada type T, and where the
       INTENT attribute of the corresponding dummy argument matches the
       Ada formal parameter mode; the Fortran implementation's parameter
       passing conventions are used.  For elementary types, a local copy
       is used if necessary to ensure by-copy semantics.

   26  An Ada parameter of an access-to-subprogram type is passed as a
       reference to a Fortran procedure whose interface corresponds to
       the designated subprogram's specification.


     NOTES
27   (17) An object of a Fortran-compatible record type, declared in a
     library package or subprogram, can correspond to a Fortran common block;
     the type also corresponds to a Fortran ``derived type''.


                                  Examples

28   Example of Interfaces.Fortran:

29  with Interfaces.Fortran;
    use Interfaces.Fortran;
    procedure Ada_Application is

30     type Fortran_Matrix is array (Integer range <>,
                                     Integer range <>) of Double_Precision;
       pragma Convention (Fortran, Fortran_Matrix);    -- stored in Fortran's
                                                       -- column-major order
       procedure Invert (Rank : in Fortran_Integer; X : in out Fortran_Matrix);
       pragma Import (Fortran, Invert);                -- a Fortran subroutine

31     Rank      : constant Fortran_Integer := 100;
       My_Matrix : Fortran_Matrix (1 .. Rank, 1 .. Rank);

32  begin

33     ...
       My_Matrix := ...;
       ...
       Invert (Rank, My_Matrix);
       ...

34  end Ada_Application;



                                   Annex C
                                 (normative)


                             Systems Programming



1   [{systems programming} {low-level programming} {real-time systems}
{embedded systems} {distributed systems} {information systems} The Systems
Programming Annex specifies additional capabilities provided for low-level
programming.  These capabilities are also required in many real-time,
embedded, distributed, and information systems.]


                            Extensions to Ada 83

        1.a   {extensions to Ada 83} This Annex is new to Ada 9X.



C.1 Access to Machine Operations

1   [This clause specifies rules regarding access to machine instructions
from within an Ada program.]

        1.a   Implementation defined:  Support for access to machine
        instructions.


                         Implementation Requirements

2   {machine code insertion} The implementation shall support machine code
insertions (see 13.8) or intrinsic subprograms (see 6.3.1) (or both).
Implementation-defined attributes shall be provided to allow the use of Ada
entities as operands.


                            Implementation Advice

3   The machine code or intrinsics support should allow access to all
operations normally available to assembly language programmers for the target
environment, including privileged instructions, if any.

        3.a   Ramification:  Of course, on a machine with protection, an
        attempt to execute a privileged instruction in user mode will
        probably trap.  Nonetheless, we want implementations to provide
        access to them so that Ada can be used to write systems programs that
        run in privileged mode.

4   {interface to assembly language} {language (interface to assembly)}
{mixed-language programs} {assembly language} The interfacing pragmas (see
Annex B) should support interface to assembler; the default assembler should
be associated with the convention identifier Assembler.

5   If an entity is exported to assembly language, then the implementation
should allocate it at an addressable location, and should ensure that it is
retained by the linking process, even if not otherwise referenced from the
Ada code.  The implementation should assume that any call to a machine code
or assembler subprogram is allowed to read or update every object that is
specified as exported.
                         Documentation Requirements

6   {documentation requirements} The implementation shall document the
overhead associated with calling machine-code or intrinsic subprograms, as
compared to a fully-inlined call, and to a regular out-of-line call.

7   The implementation shall document the types of the package
System.Machine_Code usable for machine code insertions, and the attributes to
be used in machine code insertions for references to Ada entities.

8   The implementation shall document the subprogram calling conventions
associated with the convention identifiers available for use with the
interfacing pragmas (Ada and Assembler, at a minimum), including register
saving, exception propagation, parameter passing, and function value
returning.

9   For exported and imported subprograms, the implementation shall document
the mapping between the Link_Name string, if specified, or the Ada
designator, if not, and the external link name used for such a subprogram.

        9.a   Implementation defined:  Implementation-defined aspects of
        access to machine operations.


                            Implementation Advice

10   The implementation should ensure that little or no overhead is
associated with calling intrinsic and machine-code subprograms.

11   It is recommended that intrinsic subprograms be provided for convenient
access to any machine operations that provide special capabilities or
efficiency and that are not otherwise available through the language
constructs.  Examples of such instructions include:

   12  Atomic read-modify-write operations -- e.g., test and set,
       compare and swap, decrement and test, enqueue/dequeue.

   13  Standard numeric functions -- e.g., sin, log.

   14  String manipulation operations -- e.g., translate and test.

   15  Vector operations -- e.g., compare vector against thresholds.

   16  Direct operations on I/O ports.



C.2 Required Representation Support

1   This clause specifies minimal requirements on the implementation's
support for representation items and related features.


                         Implementation Requirements

2   {recommended level of support [required in Systems Programming Annex]}
The implementation shall support at least the functionality defined by the
recommended levels of support in Section 13.



C.3 Interrupt Support

1   [This clause specifies the language-defined model for hardware interrupts
in addition to mechanisms for handling interrupts.]  {signal: see interrupt}


                              Dynamic Semantics

2   {interrupt} [An interrupt represents a class of events that are detected
by the hardware or the system software.]  {occurrence (of an interrupt)}
Interrupts are said to occur.  An occurrence of an interrupt is separable
into generation and delivery.  {generation (of an interrupt)} Generation of
an interrupt is the event in the underlying hardware or system that makes the
interrupt available to the program.  {delivery (of an interrupt)} Delivery is
the action that invokes part of the program as response to the interrupt
occurrence.  {pending interrupt occurrence} Between generation and delivery,
the interrupt occurrence [(or interrupt)] is pending.  {blocked interrupt}
Some or all interrupts may be blocked.  When an interrupt is blocked, all
occurrences of that interrupt are prevented from being delivered.  {attaching
(to an interrupt)} {reserved interrupt} Certain interrupts are reserved.  The
set of reserved interrupts is implementation defined.  A reserved interrupt
is either an interrupt for which user-defined handlers are not supported, or
one which already has an attached handler by some other implementation-
defined means.  {interrupt handler} Program units can be connected to
non-reserved interrupts.  While connected, the program unit is said to be
attached to that interrupt.  The execution of that program unit, the
interrupt handler, is invoked upon delivery of the interrupt occurrence.

        2.a   Implementation defined:  Implementation-defined aspects of
        interrupts.

        2.b   To be honest:  As an obsolescent feature, interrupts may be
        attached to task entries by an address clause.  See J.7.1.

3   While a handler is attached to an interrupt, it is called once for each
delivered occurrence of that interrupt.  While the handler executes, the
corresponding interrupt is blocked.

4   While an interrupt is blocked, all occurrences of that interrupt are
prevented from being delivered.  Whether such occurrences remain pending or
are lost is implementation defined.

5   {default treatment} Each interrupt has a default treatment which
determines the system's response to an occurrence of that interrupt when no
user-defined handler is attached.  The set of possible default treatments is
implementation defined, as is the method (if one exists) for configuring the
default treatments for interrupts.

6   An interrupt is delivered to the handler (or default treatment) that is
in effect for that interrupt at the time of delivery.

7   An exception propagated from a handler that is invoked by an interrupt
has no effect.

8   [If the Ceiling_Locking policy (see D.3) is in effect, the interrupt
handler executes with the active priority that is the ceiling priority of the
corresponding protected object.]


                         Implementation Requirements

9   The implementation shall provide a mechanism to determine the minimum
stack space that is needed for each interrupt handler and to reserve that
space for the execution of the handler. [This space should accommodate nested
invocations of the handler where the system permits this.]

10   If the hardware or the underlying system holds pending interrupt
occurrences, the implementation shall provide for later delivery of these
occurrences to the program.

11   If the Ceiling_Locking policy is not in effect, the implementation shall
provide means for the application to specify whether interrupts are to be
blocked during protected actions.


                         Documentation Requirements

12   {documentation requirements} The implementation shall document the
following items:

        12.a   Discussion:  This information may be different for different
        forms of interrupt handlers.

   13  For each interrupt, which interrupts are blocked from delivery
       when a handler attached to that interrupt executes (either as a
       result of an interrupt delivery or of an ordinary call on a
       procedure of the corresponding protected object).

   14  Any interrupts that cannot be blocked, and the effect of
       attaching handlers to such interrupts, if this is permitted.

   15  Which run-time stack an interrupt handler uses when it executes
       as a result of an interrupt delivery; if this is configurable,
       what is the mechanism to do so; how to specify how much space to
       reserve on that stack.

   16  Any implementation- or hardware-specific activity that happens
       before a user-defined interrupt handler gets control (e.g.,
       reading device registers, acknowledging devices).

   17  Any timing or other limitations imposed on the execution of
       interrupt handlers.

   18  The state (blocked/unblocked) of the non-reserved interrupts when
       the program starts; if some interrupts are unblocked, what is the
       mechanism a program can use to protect itself before it can
       attach the corresponding handlers.

   19  Whether the interrupted task is allowed to resume execution
       before the interrupt handler returns.

   20  The treatment of interrupt occurrences that are generated while
       the interrupt is blocked; i.e., whether one or more occurrences
       are held for later delivery, or all are lost.

   21  Whether predefined or implementation-defined exceptions are
       raised as a result of the occurrence of any interrupt, and the
       mapping between the machine interrupts (or traps) and the
       predefined exceptions.  {94-4768.l}

   22  On a multi-processor, the rules governing the delivery of an
       interrupt to a particular processor.


                         Implementation Permissions

23   If the underlying system or hardware does not allow interrupts to be
blocked, then no blocking is required [as part of the execution of
subprograms of a protected object whose one of its subprograms is an
interrupt handler].

24   In a multi-processor with more than one interrupt subsystem, it is
implementation defined whether (and how) interrupt sources from separate
subsystems share the same Interrupt_ID type (see C.3.2).  {94-4761.q}

        24.a   Discussion:  This issue is tightly related to the issue of
        scheduling on a multi-processor.  In a sense, if a particular
        interrupt source is not available to all processors, the system is
        not truly homogeneous.

        24.b   One way to approach this problem is to assign sub-ranges
        within Interrupt_ID to each interrupt subsystem, such that
        ``similar'' interrupt sources (e.g. a timer) in different subsystems
        get a distinct id.

In particular, the meaning of a blocked or pending interrupt may then be
applicable to one processor only.

25   Implementations are allowed to impose timing or other limitations on the
execution of interrupt handlers.

        25.a   Reason:  These limitations are often necessary to ensure
        proper behavior of the implementation.

26   Other forms of handlers are allowed to be supported, in which case, the
rules of this subclause should be adhered to.

27   The active priority of the execution of an interrupt handler is allowed
to vary from one occurrence of the same interrupt to another.


                            Implementation Advice

28   If the Ceiling_Locking policy is not in effect, the implementation
should provide means for the application to specify which interrupts are to
be blocked during protected actions, if the underlying system allows for a
finer-grain control of interrupt blocking.


     NOTES
29   (1) The default treatment for an interrupt can be to keep the interrupt
     pending or to deliver it to an implementation-defined handler.  Examples
     of actions that an implementation-defined handler is allowed to perform
     include aborting the partition, ignoring (i.e., discarding occurrences
     of) the interrupt, or queuing one or more occurrences of the interrupt
     for possible later delivery when a user-defined handler is attached to
     that interrupt.

30   (2) It is a bounded error to call Task_Identification.Current_Task (see
     C.7.1) from an interrupt handler.

31   (3) The rule that an exception propagated from an interrupt handler has
     no effect is modeled after the rule about exceptions propagated out of
     task bodies.



C.3.1 Protected Procedure Handlers

                                   Syntax

    1   The form of a pragma Interrupt_Handler is as follows:


2     pragma Interrupt_Handler(handler_name);

    3   The form of a pragma Attach_Handler is as follows:


4     pragma Attach_Handler(handler_name, expression);


                            Name Resolution Rules

5   For the Interrupt_Handler and Attach_Handler pragmas, the handler_name
shall resolve to denote a protected procedure with a parameterless profile.

6   For the Attach_Handler pragma, the expected type for the expression is
Interrupts.Interrupt_ID (see C.3.2).


                               Legality Rules

7   The Attach_Handler pragma is only allowed immediately within the
protected_definition where the corresponding subprogram is declared.  The
corresponding protected_type_declaration or single_protected_declaration
shall be a library level declaration.

        7.a   Discussion:  In the case of a protected_type_declaration, an
        object_declaration of an object of that type need not be at library
        level.

8   The Interrupt_Handler pragma is only allowed immediately within a
protected_definition.  The corresponding protected_type_declaration shall be
a library level declaration.  In addition, any object_declaration of such a
type shall be a library level declaration.


                              Dynamic Semantics

9   If the pragma Interrupt_Handler appears in a protected_definition, then
the corresponding procedure can be attached dynamically, as a handler, to
interrupts (see C.3.2).  [Such procedures are allowed to be attached to
multiple interrupts.]

10   {creation (of a protected object)} {initialization (of a protected
object)} The expression in the Attach_Handler pragma [as evaluated at object
creation time] specifies an interrupt.  As part of the initialization of that
object, if the Attach_Handler pragma is specified, the handler procedure is
attached to the specified interrupt.  {Reserved_Check [partial]} {check,
language-defined (Reserved_Check)} A check is made that the corresponding
interrupt is not reserved.  {Program_Error (raised by failure of run-time
check)} Program_Error is raised if the check fails, and the existing
treatment for the interrupt is not affected.

11   {initialization (of a protected object)} {Ceiling_Check [partial]}
{check, language-defined (Ceiling_Check)} If the Ceiling_Locking policy (see
D.3) is in effect then upon the initialization of a protected object that
either an Attach_Handler or Interrupt_Handler pragma applies to one of its
procedures, a check is made that the ceiling priority defined in the
protected_definition is in the range of System.Interrupt_Priority.  {Program_
Error (raised by failure of run-time check)} If the check fails, Program_
Error is raised.

12   {finalization (of a protected object)} When a protected object is
finalized, for any of its procedures that are attached to interrupts, the
handler is detached.  If the handler was attached by a procedure in the
Interrupts package or if no user handler was previously attached to the
interrupt, the default treatment is restored.  Otherwise, [that is, if an
Attach_Handler pragma was used,] the previous handler is restored.

        12.a   Discussion:  Since only library-level protected procedures can
        be attached as handlers using the Interrupts package, the
        finalization discussed above occurs only as part of the finalization
        of all library-level packages in a partition.

13   When a handler is attached to an interrupt, the interrupt is blocked
[(subject to the Implementation Permission in C.3)] during the execution of
every protected action on the protected object containing the handler.


                             Erroneous Execution

14   {erroneous execution} If the Ceiling_Locking policy (see D.3) is in
effect and an interrupt is delivered to a handler, and the interrupt hardware
priority is higher than the ceiling priority of the corresponding protected
object, the execution of the program is erroneous.


                                   Metrics

15   {metrics} The following metric shall be documented by the
implementation:

   16  The worst case overhead for an interrupt handler that is a
       parameterless protected procedure, in clock cycles.  This is the
       execution time not directly attributable to the handler procedure
       or the interrupted execution.  It is estimated as C - (A+B),
       where A is how long it takes to complete a given sequence of
       instructions without any interrupt, B is how long it takes to
       complete a normal call to a given protected procedure, and C is
       how long it takes to complete the same sequence of instructions
       when it is interrupted by one execution of the same procedure
       called via an interrupt.

 16.a   Implementation Note:  The instruction sequence and interrupt
        handler used to measure interrupt handling overhead should be
        chosen so as to maximize the execution time cost due to cache
        misses.  For example, if the processor has cache memory and the
        activity of an interrupt handler could invalidate the contents
        of cache memory, the handler should be written such that it
        invalidates all of the cache memory.


                         Implementation Permissions

17   When the pragmas Attach_Handler or Interrupt_Handler apply to a
protected procedure, the implementation is allowed to impose implementation-
defined restrictions on the corresponding protected_type_declaration and
protected_body.

        17.a   Ramification:  The restrictions may be on the constructs that
        are allowed within them, and on ordinary calls (i.e. not via
        interrupts) on protected operations in these protected objects.

18   An implementation may use a different mechanism for invoking a protected
procedure in response to a hardware interrupt than is used for a call to that
protected procedure from a task.

        18.a   Discussion:  This is despite the fact that the priority of an
        interrupt handler (see D.1) is modeled after a hardware task calling
        the handler.

19   {notwithstanding} Notwithstanding what this subclause says elsewhere,
the Attach_Handler and Interrupt_Handler pragmas are allowed to be used for
other, implementation defined, forms of interrupt handlers.

        19.a   Ramification:  For example, if an implementation wishes to
        allow interrupt handlers to have parameters, it is allowed to do so
        via these pragmas; it need not invent implementation-defined pragmas
        for the purpose.


                            Implementation Advice

20   Whenever possible, the implementation should allow interrupt handlers to
be called directly by the hardware.

21   Whenever practical, the implementation should detect violations of any
implementation-defined restrictions before run time.


     NOTES
22   (4) The Attach_Handler pragma can provide static attachment of handlers
     to interrupts if the implementation supports preelaboration of protected
     objects.  (See C.4.)

23   (5) The ceiling priority of a protected object that one of its
     procedures is attached to an interrupt should be at least as high as the
     highest processor priority at which that interrupt will ever be
     delivered.

24   (6) Protected procedures can also be attached dynamically to interrupts
     via operations declared in the predefined package Interrupts.

25   (7) An example of a possible implementation-defined restriction is
     disallowing the use of the standard storage pools within the body of a
     protected procedure that is an interrupt handler.



C.3.2 The Package Interrupts

                              Static Semantics

1   The following language-defined packages exist:

2   with System;
    package Ada.Interrupts is
       type Interrupt_ID is implementation-defined;
       type Parameterless_Handler is
          access protected procedure;

3


4      function Is_Reserved (Interrupt : Interrupt_ID)
          return Boolean;

5      function Is_Attached (Interrupt : Interrupt_ID)
          return Boolean;

6      function Current_Handler (Interrupt : Interrupt_ID)
          return Parameterless_Handler;

7      procedure Attach_Handler
          (New_Handler : in Parameterless_Handler;
           Interrupt   : in Interrupt_ID);

8      procedure Exchange_Handler
          (Old_Handler : out Parameterless_Handler;
           New_Handler : in Parameterless_Handler;
           Interrupt   : in Interrupt_ID);

9      procedure Detach_Handler
          (Interrupt : in Interrupt_ID);

10     function Reference(Interrupt : Interrupt_ID)
          return System.Address;

11  private
       ... -- not specified by the language
    end Ada.Interrupts;

12

    package Ada.Interrupts.Names is
       implementation-defined : constant Interrupt_ID :=
         implementation-defined;
          . . .
       implementation-defined : constant Interrupt_ID :=
         implementation-defined;
    end Ada.Interrupts.Names;


                              Dynamic Semantics

13   The Interrupt_ID type is an implementation-defined discrete type used to
identify interrupts.

14   The Is_Reserved function returns True if and only if the specified
interrupt is reserved.

15   The Is_Attached function returns True if and only if a user-specified
interrupt handler is attached to the interrupt.

16   The Current_Handler function returns a value that represents the
attached handler of the interrupt.  If no user-defined handler is attached to
the interrupt, Current_Handler returns a value that designates the default
treatment; calling Attach_Handler or Exchange_Handler with this value
restores the default treatment.

17   The Attach_Handler procedure attaches the specified handler to the
interrupt, overriding any existing treatment (including a user handler) in
effect for that interrupt.  If New_Handler is null, the default treatment is
restored.  {Program_Error (raised by failure of run-time check)} If New_
Handler designates a protected procedure to which the pragma Interrupt_
Handler does not apply, Program_Error is raised.  In this case, the operation
does not modify the existing interrupt treatment.

18   The Exchange_Handler procedure operates in the same manner as Attach_
Handler with the addition that the value returned in Old_Handler designates
the previous treatment for the specified interrupt.

        18.a   Ramification:  Calling Attach_Handler or Exchange_Handler with
        this value for New_Handler restores the previous handler.

19   The Detach_Handler procedure restores the default treatment for the
specified interrupt.

20   For all operations defined in this package that take a parameter of type
Interrupt_ID, with the exception of Is_Reserved and Reference, a check is
made that the specified interrupt is not reserved.  {Program_Error (raised by
failure of run-time check)} Program_Error is raised if this check fails.

21   If, by using the Attach_Handler, Detach_Handler, or Exchange_Handler
procedures, an attempt is made to detach a handler that was attached
statically (using the pragma Attach_Handler), the handler is not detached and
Program_Error is raised.  {Program_Error (raised by failure of run-time
check)}

22   The Reference function returns a value of type System.Address that can
be used to attach a task entry, via an address clause (see J.7.1) to the
interrupt specified by Interrupt.  This function raises Program_Error if
attaching task entries to interrupts (or to this particular interrupt) is not
supported.  {Program_Error (raised by failure of run-time check)}


                         Implementation Requirements

23   At no time during attachment or exchange of handlers shall the current
handler of the corresponding interrupt be undefined.


                         Documentation Requirements

24   {documentation requirements} If the Ceiling_Locking policy (see D.3) is
in effect the implementation shall document the default ceiling priority
assigned to a protected object that contains either the Attach_Handler or
Interrupt_Handler pragmas, but not the Interrupt_Priority pragma.  [This
default need not be the same for all interrupts.]


                            Implementation Advice

25   If implementation-defined forms of interrupt handler procedures are
supported, such as protected procedures with parameters, then for each such
form of a handler, a type analogous to Parameterless_Handler should be
specified in a child package of Interrupts, with the same operations as in
the predefined package Interrupts.


     NOTES
26   (8) The package Interrupts.Names contains implementation-defined names
     (and constant values) for the interrupts that are supported by the
     implementation.


                                  Examples

27   Example of interrupt handlers:

28  Device_Priority : constant
      array (1..5) of System.Interrupt_Priority := ( ... );
    protected type Device_Interface
      (Int_ID : Ada.Interrupts.Interrupt_ID) is
      procedure Handler;
      pragma Attach_Handler(Handler, Int_ID);
      ...
      pragma Interrupt_Priority(Device_Priority(Int_ID));
    end Device_Interface;
      ...
    Device_1_Driver : Device_Interface(1);
      ...
    Device_5_Driver : Device_Interface(5);
      ...



C.4 Preelaboration Requirements

1   [This clause specifies additional implementation and documentation
requirements for the Preelaborate pragma (see 10.2.1).]


                         Implementation Requirements

2   The implementation shall not incur any run-time overhead for the
elaboration checks of subprograms and protected_bodies declared in
preelaborated library units.

3   The implementation shall not execute any memory write operations after
load time for the elaboration of constant objects declared immediately within
the declarative region of a preelaborated library package, so long as the
subtype and initial expression (or default initial expressions if initialized
by default) of the object_declaration satisfy the following restrictions.
{load time} The meaning of load time is implementation defined.
        3.a   Discussion:  On systems where the image of the partition is
        initially copied from disk to RAM, or from ROM to RAM, prior to
        starting execution of the partition, the intention is that ``load
        time'' consist of this initial copying step.  On other systems, load
        time and run time might actually be interspersed.

    4  Any subtype_mark denotes a statically constrained subtype, with
       statically constrained subcomponents, if any;

    5  any constraint is a static constraint;

    6  any allocator is for an access-to-constant type;

    7  any uses of predefined operators appear only within static
       expressions;

    8  any primaries that are names, other than attribute_references for
       the Access or Address attributes, appear only within static
       expressions;

 8.a    Ramification:  This cuts out attribute_references that are not
        static, except for Access and Address.

    9  any name that is not part of a static expression is an expanded
       name or direct_name that statically denotes some entity;

 9.a    Ramification:  This cuts out function_calls and type_conversions
        that are not static, including calls on attribute functions like
        'Image and 'Value.

   10  any discrete_choice of an array_aggregate is static;

   11  no language-defined check associated with the elaboration of the
       object_declaration can fail.

 11.a   Reason:  The intent is that aggregates all of whose scalar
        subcomponents are static, and all of whose access subcomponents
        are null, allocators for access-to-constant types, or X'Access,
        will be supported with no run-time code generated.


                         Documentation Requirements

12   {documentation requirements} The implementation shall document any
circumstances under which the elaboration of a preelaborated package causes
code to be executed at run time.

13   The implementation shall document whether the method used for
initialization of preelaborated variables allows a partition to be restarted
without reloading.

        13.a   Implementation defined:  Implementation-defined aspects of
        preelaboration.

        13.b   Discussion:  This covers the issue of the RTS itself being
        restartable, so that need not be a separate Documentation
        Requirement.


                            Implementation Advice

14   It is recommended that preelaborated packages be implemented in such a
way that there should be little or no code executed at run time for the
elaboration of entities not already covered by the Implementation
Requirements.



C.5 Pragma Discard_Names

1   [A pragma Discard_Names may be used to request a reduction in storage
used for the names of certain entities.]


                                   Syntax

    2   The form of a pragma Discard_Names is as follows:


3     pragma Discard_Names[([On => ] local_name)];

    4   A pragma Discard_Names is allowed only immediately within a
    declarative_part, immediately within a package_specification, or as a
    configuration pragma.


                               Legality Rules

5   The local_name (if present) shall denote a non-derived enumeration
[first] subtype, a tagged [first] subtype, or an exception.  The pragma
applies to the type or exception.  Without a local_name, the pragma applies
to all such entities declared after the pragma, within the same declarative
region.  Alternatively, the pragma can be used as a configuration pragma.  If
the pragma applies to a type, then it applies also to all descendants of the
type.  {94-4894.a}


                              Static Semantics

6   {representation pragma [Discard_Names]} {pragma, representation [Discard_
Names]} If a local_name is given, then a pragma Discard_Names is a
representation pragma.

7   If the pragma applies to an enumeration type, then the semantics of the
Wide_Image and Wide_Value attributes are implementation defined for that
type; [the semantics of Image and Value are still defined in terms of Wide_
Image and Wide_Value.]  In addition, the semantics of Text_IO.Enumeration_IO
are implementation defined.  If the pragma applies to a tagged type, then the
semantics of the Tags.Expanded_Name function are implementation defined for
that type.  If the pragma applies to an exception, then the semantics of the
Exceptions.Exception_Name function are implementation defined for that
exception.  {94-4894.a} {94-4902.a} {94-4904.a} {94-4905.a} {94-4906.a}

        7.a   Implementation defined:  The semantics of pragma Discard_Names.

        7.b   Ramification:  The Width attribute is still defined in terms of
        Image.

        7.c   The semantics of S'Wide_Image and S'Wide_Value are implemen-
        tation defined for any subtype of an enumeration type to which the
        pragma applies.  (The pragma actually names the first subtype, of
        course.)


                            Implementation Advice

8   If the pragma applies to an entity, then the implementation should reduce
the amount of storage used for storing names associated with that entity.

        8.a   Reason:  A typical implementation of the Image attribute for
        enumeration types is to store a table containing the names of all the
        enumeration literals.  Pragma Discard_Names allows the implementation
        to avoid storing such a table without having to prove that the Image
        attribute is never used (which can be difficult in the presence of
        separate compilation).

        8.b   We did not specify the semantics of the Image attribute in the
        presence of this pragma because different semantics might be
        desirable in different situations.  In some cases, it might make
        sense to use the Image attribute to print out a useful value that can
        be used to identify the entity given information in compiler-
        generated listings.  In other cases, it might make sense to get an
        error at compile time or at run time.  In cases where memory is
        plentiful, the simplest implementation makes sense: ignore the
        pragma.  Implementations that are capable of avoiding the extra
        storage in cases where the Image attribute is never used might also
        wish to ignore the pragma.

        8.c   The same applies to the Tags.Expanded_Name and Exceptions.-
        Exception_Name functions.



C.6 Shared Variable Control

1   [This clause specifies representation pragmas that control the use of
shared variables.]


                                   Syntax

    2   The form for pragmas Atomic, Volatile, Atomic_Components, and
    Volatile_Components is as follows:


3     pragma Atomic(local_name);

4     pragma Volatile(local_name);

5     pragma Atomic_Components(array_local_name);

6     pragma Volatile_Components(array_local_name);


7   {atomic} An atomic type is one to which a pragma Atomic applies.  An
atomic object (including a component) is one to which a pragma Atomic
applies, or a component of an array to which a pragma Atomic_Components
applies, or any object of an atomic type.

8   {volatile} A volatile type is one to which a pragma Volatile applies.  A
volatile object (including a component) is one to which a pragma Volatile
applies, or a component of an array to which a pragma Volatile_Components
applies, or any object of a volatile type.  In addition, every atomic type or
object is also defined to be volatile.  Finally, if an object is volatile,
then so are all of its subcomponents [(the same does not apply to atomic)].


                            Name Resolution Rules

9   The local_name in an Atomic or Volatile pragma shall resolve to denote
either an object_declaration, a non-inherited component_declaration, or a
full_type_declaration.  The array_local_name in an Atomic_Components or
Volatile_Components pragma shall resolve to denote the declaration of an
array type or an array object of an anonymous type.


                               Legality Rules

10   {indivisible} It is illegal to apply either an Atomic or Atomic_
Components pragma to an object or type if the implementation cannot support
the indivisible reads and updates required by the pragma (see below).

11   It is illegal to specify the Size attribute of an atomic object, the
Component_Size attribute for an array type with atomic components, or the
layout attributes of an atomic component, in a way that prevents the
implementation from performing the required indivisible reads and updates.

12   If an atomic object is passed as a parameter, then the type of the
formal parameter shall either be atomic or allow pass by copy [(that is, not
be a nonatomic by-reference type)].  If an atomic object is used as an actual
for a generic formal object of mode in out, then the type of the generic
formal object shall be atomic.  If the prefix of an attribute_reference for
an Access attribute denotes an atomic object [(including a component)], then
the designated type of the resulting access type shall be atomic.  If an
atomic type is used as an actual for a generic formal derived type, then the
ancestor of the formal type shall be atomic or allow pass by copy.
Corresponding rules apply to volatile objects and types.

13   If a pragma Volatile, Volatile_Components, Atomic, or Atomic_Components
applies to a stand-alone constant object, then a pragma Import shall also
apply to it.

        13.a   Ramification:  Hence, no initialization expression is allowed
        for such a constant.  Note that a constant that is atomic or volatile
        because of its type is allowed.

        13.b   Reason:  Stand-alone constants that are explicitly specified
        as Atomic or Volatile only make sense if they are being manipulated
        outside the Ada program.  From the Ada perspective the object is
        read-only.  Nevertheless, if imported and atomic or volatile, the
        implementation should presume it might be altered externally.  For an
        imported stand-alone constant that is not atomic or volatile, the
        implementation can assume that it will not be altered.


                              Static Semantics

14   {representation pragma [Atomic]} {pragma, representation [Atomic]}
{representation pragma [Volatile]} {pragma, representation [Volatile]}
{representation pragma [Atomic_Components]} {pragma, representation [Atomic_
Components]} {representation pragma [Volatile_Components]} {pragma,
representation [Volatile_Components]} These pragmas are representation
pragmas (see 13.1).


                              Dynamic Semantics

15   For an atomic object (including an atomic component) all reads and
updates of the object as a whole are indivisible.

16   For a volatile object all reads and updates of the object as a whole are
performed directly to memory.

        16.a   Implementation Note:  This precludes any use of register
        temporaries, caches, and other similar optimizations for that object.

17   {sequential (actions)} Two actions are sequential (see 9.10) if each is
the read or update of the same atomic object.

18   {by-reference type [atomic or volatile]} If a type is atomic or volatile
and it is not a by-copy type, then the type is defined to be a by-reference
type.  If any subcomponent of a type is atomic or volatile, then the type is
defined to be a by-reference type.

19   If an actual parameter is atomic or volatile, and the corresponding
formal parameter is not, then the parameter is passed by copy.

        19.a   Implementation Note:  Note that in the case where such a
        parameter is normally passed by reference, a copy of the actual will
        have to be produced at the call-site, and a pointer to the copy
        passed to the formal parameter.  If the actual is atomic, any copying
        has to use indivisible read on the way in, and indivisible write on
        the way out.

        19.b   Reason:  It has to be known at compile time whether an atomic
        or a volatile parameter is to be passed by copy or by reference.  For
        some types, it is unspecified whether parameters are passed by copy
        or by reference.  The above rules further specify the parameter
        passing rules involving atomic and volatile types and objects.


                         Implementation Requirements

20   {external effect [volatile/atomic objects]} The external effect of a
program (see 1.1.3) is defined to include each read and update of a volatile
or atomic object.  The implementation shall not generate any memory reads or
updates of atomic or volatile objects other than those specified by the
program.

        20.a   Discussion:  The presumption is that volatile or atomic
        objects might reside in an ``active'' part of the address space where
        each read has a potential side-effect, and at the very least might
        deliver a different value.

        20.b   The rule above and the definition of external effect are
        intended to prevent (at least) the following incorrect optimizations,
        where V is a volatile variable:

         20.c  X:= V; Y:=V; cannot be allowed to be translated as Y:=V;
               X:=V;

         20.d  Deleting redundant loads: X:= V; X:= V; shall read the
               value of V from memory twice.

         20.e  Deleting redundant stores: V:= X; V:= X; shall write into
               V twice.

         20.f  Extra stores: V:= X+Y; should not translate to something
               like V:= X; V:= V+Y;

         20.g  Extra loads: X:= V; Y:= X+Z; X:=X+B; should not translate
               to something like Y:= V+Z; X:= V+B;

         20.h  Reordering of loads from volatile variables: X:= V1; Y:=
               V2; (whether or not V1 = V2) should not translate to Y:=
               V2; X:= V1;

         20.i  Reordering of stores to volatile variables: V1:= X; V2:=
               X; should not translate to V2:=X; V1:= X;

21   If a pragma Pack applies to a type any of whose subcomponents are
atomic, the implementation shall not pack the atomic subcomponents more
tightly than that for which it can support indivisible reads and updates.

        21.a   Implementation Note:  A warning might be appropriate if no
        packing whatsoever can be achieved.


     NOTES
22   (9) An imported volatile or atomic constant behaves as a constant (i.e.
     read-only) with respect to other parts of the Ada program, but can still
     be modified by an ``external source.''


                        Incompatibilities With Ada 83

        22.a   {incompatibilities with Ada 83} Pragma Atomic replaces Ada
        83's pragma Shared.  The name ``Shared'' was confusing, because the
        pragma was not used to mark variables as shared.



C.7 Task Identification and Attributes

1   [This clause describes operations and attributes that can be used to
obtain the identity of a task.  In addition, a package that associates
user-defined information with a task is defined.]



C.7.1 The Package Task_Identification

                              Static Semantics

1   The following language-defined library package exists:

2   package Ada.Task_Identification is
       type Task_ID is private;
       Null_Task_ID : constant Task_ID;
       function  "=" (Left, Right : Task_ID) return Boolean;

3      function  Image        (T : Task_ID) return String;
       function  Current_Task return Task_ID;
       procedure Abort_Task   (T : in out Task_ID);

4      function  Is_Terminated(T : Task_ID) return Boolean;
       function  Is_Callable  (T : Task_ID) return Boolean;
    private
       ... -- not specified by the language
    end Ada.Task_Identification;


                              Dynamic Semantics

5   A value of the type Task_ID identifies an existent task.  The constant
Null_Task_ID does not identify any task.  Each object of the type Task_ID is
default initialized to the value of Null_Task_ID.

6   The function "=" returns True if and only if Left and Right identify the
same task or both have the value Null_Task_ID.

7   The function Image returns an implementation-defined string that
identifies T. If T equals Null_Task_ID, Image returns an empty string.

        7.a   Implementation defined:  The result of the Task_
        Identification.Image attribute.

8   The function Current_Task returns a value that identifies the calling
task.

9   The effect of Abort_Task is the same as the abort_statement for the task
identified by T. [In addition, if T identifies the environment task, the
entire partition is aborted, See E.1.]

10   The functions Is_Terminated and Is_Callable return the value of the
corresponding attribute of the task identified by T.

11   For a prefix T that is of a task type [(after any implicit
dereference)], the following attribute is defined:
12  T'Identity
                Yields a value of the type Task_ID that identifies the task
                denoted by T.

13   For a prefix E that denotes an entry_declaration, the following
attribute is defined:

14  E'Caller
                Yields a value of the type Task_ID that identifies the task
                whose call is now being serviced.  Use of this attribute is
                allowed only inside an entry_body or accept_statement
                corresponding to the entry_declaration denoted by E.

15   {Program_Error (raised by failure of run-time check)} Program_Error is
raised if a value of Null_Task_ID is passed as a parameter to Abort_Task, Is_
Terminated, and Is_Callable.

16   {potentially blocking operation [Abort_Task]} {blocking, potentially
[Abort_Task]} Abort_Task is a potentially blocking operation (see 9.5.1).


                          Bounded (Run-Time) Errors

17   {bounded error} It is a bounded error to call the Current_Task function
from an entry body or an interrupt handler.  {Program_Error (raised by
failure of run-time check)} Program_Error is raised, or an implementation-
defined value of the type Task_ID is returned.

        17.a   Implementation defined:  The value of Current_Task when in a
        protected entry or interrupt handler.

        17.b   Implementation Note:  This value could be Null_Task_ID, or the
        ID of some user task, or that of an internal task created by the
        implementation.


                             Erroneous Execution

18   {erroneous execution} If a value of Task_ID is passed as a parameter to
any of the operations declared in this package (or any language-defined child
of this package), and the corresponding task object no longer exists, the
execution of the program is erroneous.


                         Documentation Requirements

19   {documentation requirements} The implementation shall document the
effect of calling Current_Task from an entry body or interrupt handler.

        19.a   Implementation defined:  The effect of calling Current_Task
        from an entry body or interrupt handler.


     NOTES
20   (10) This package is intended for use in writing user-defined task
     scheduling packages and constructing server tasks.  Current_Task can be
     used in conjunction with other operations requiring a task as an
     argument such as Set_Priority (see D.5).

21   (11) The function Current_Task and the attribute Caller can return a
     Task_ID value that identifies the environment task.



C.7.2 The Package Task_Attributes

                              Static Semantics

1   The following language-defined generic library package exists:

2   with Ada.Task_Identification; use Ada.Task_Identification;
    generic
       type Attribute is private;
       Initial_Value : in Attribute;
    package Ada.Task_Attributes is

3      type Attribute_Handle is access all Attribute;

4      function Value(T : Task_ID := Current_Task)
         return Attribute;

5      function Reference(T : Task_ID := Current_Task)
         return Attribute_Handle;

6      procedure Set_Value(Val : in Attribute;
                                 T : in Task_ID := Current_Task);
       procedure Reinitialize(T : in Task_ID := Current_Task);

7   end Ada.Task_Attributes;


                              Dynamic Semantics

8   When an instance of Task_Attributes is elaborated in a given active
partition, an object of the actual type corresponding to the formal type
Attribute is implicitly created for each task (of that partition) that exists
and is not yet terminated.  This object acts as a user-defined attribute of
the task.  A task created previously in the partition and not yet terminated
has this attribute from that point on.  Each task subsequently created in the
partition will have this attribute when created.  In all these cases, the
initial value of the given attribute is Initial_Value.

9   The Value operation returns the value of the corresponding attribute of
T.

10   The Reference operation returns an access value that designates the
corresponding attribute of T.

11   The Set_Value operation performs any finalization on the old value of
the attribute of T and assigns Val to that attribute (see 5.2 and 7.6).

12   The effect of the Reinitialize operation is the same as Set_Value where
the Val parameter is replaced with Initial_Value.

        12.a   Implementation Note:  In most cases, the attribute memory can
        be reclaimed at this point.

13   {Tasking_Error (raised by failure of run-time check)} For all the
operations declared in this package, Tasking_Error is raised if the task
identified by T is terminated.  {Program_Error (raised by failure of run-time
check)} Program_Error is raised if the value of T is Null_Task_ID.


                             Erroneous Execution

14   {erroneous execution} It is erroneous to dereference the access value
returned by a given call on Reference after a subsequent call on Reinitialize
for the same task attribute, or after the associated task terminates.

        14.a   Reason:  This allows the storage to be reclaimed for the
        object associated with an attribute upon Reinitialize or task
        termination.

15   If a value of Task_ID is passed as a parameter to any of the operations
declared in this package and the corresponding task object no longer exists,
the execution of the program is erroneous.


                         Implementation Requirements

16   The implementation shall perform each of the above operations for a
given attribute of a given task atomically with respect to any other of the
above operations for the same attribute of the same task.

        16.a   Ramification:  Hence, other than by dereferencing an access
        value returned by Reference, an attribute of a given task can be
        safely read and updated concurrently by multiple tasks.

17   When a task terminates, the implementation shall finalize all attributes
of the task, and reclaim any other storage associated with the attributes.


                         Documentation Requirements

18   {documentation requirements} The implementation shall document the limit
on the number of attributes per task, if any, and the limit on the total
storage for attribute values per task, if such a limit exists.

19   In addition, if these limits can be configured, the implementation shall
document how to configure them.

        19.a   Implementation defined:  Implementation-defined aspects of
        Task_Attributes.


                                   Metrics

20   {metrics} The implementation shall document the following metrics: A
task calling the following subprograms shall execute in a sufficiently high
priority as to not be preempted during the measurement period.  This period
shall start just before issuing the call and end just after the call
completes.  If the attributes of task T are accessed by the measurement
tests, no other task shall access attributes of that task during the
measurement period.  For all measurements described here, the Attribute type
shall be a scalar whose size is equal to the size of the predefined integer
size.  For each measurement, two cases shall be documented: one where the
accessed attributes are of the calling task [(that is, the default value for
the T parameter is used)], and the other, where T identifies another,
non-terminated, task.

21   The following calls (to subprograms in the Task_Attributes package)
shall be measured:

   22  a call to Value, where the return value is Initial_Value;

   23  a call to Value, where the return value is not equal to Initial_
       Value;

   24  a call to Reference, where the return value designates a value
       equal to Initial_Value;

   25  a call to Reference, where the return value designates a value
       not equal to Initial_Value;

   26  a call to Set_Value where the Val parameter is not equal to
       Initial_Value and the old attribute value is equal to Initial_
       Value.

   27  a call to Set_Value where the Val parameter is not equal to
       Initial_Value and the old attribute value is not equal to
       Initial_Value.


                         Implementation Permissions

28   An implementation need not actually create the object corresponding to a
task attribute until its value is set to something other than that of
Initial_Value, or until Reference is called for the task attribute.
Similarly, when the value of the attribute is to be reinitialized to that of
Initial_Value, the object may instead be finalized and its storage reclaimed,
to be recreated when needed later.  While the object does not exist, the
function Value may simply return Initial_Value, rather than implicitly
creating the object.

        28.a   Discussion:  The effect of this permission can only be
        observed if the assignment operation for the corresponding type has
        side-effects.

        28.b   Implementation Note:  This permission means that even though
        every task has every attribute, storage need only be allocated for
        those attributes that have been Reference'd or set to a value other
        than that of Initial_Value.

29   An implementation is allowed to place restrictions on the maximum number
of attributes a task may have, the maximum size of each attribute, and the
total storage size allocated for all the attributes of a task.


                            Implementation Advice

30   Some implementations are targeted to domains in which memory use at run
time must be completely deterministic.  For such implementations, it is
recommended that the storage for task attributes will be pre-allocated
statically and not from the heap.  This can be accomplished by either placing
restrictions on the number and the size of the task's attributes, or by using
the pre-allocated storage for the first N attribute objects, and the heap for
the others.  In the latter case, N should be documented.


     NOTES
31   (12) An attribute always exists (after instantiation), and has the
     initial value.  It need not occupy memory until the first operation that
     potentially changes the attribute value.  The same holds true after
     Reinitialize.

32   (13) The result of the Reference function should be used with care; it
     is always safe to use that result in the task body whose attribute is
     being accessed.  However, when the result is being used by another task,
     the programmer must make sure that the task whose attribute is being
     accessed is not yet terminated.  Failing to do so could make the program
     execution erroneous.

33   (14) As specified in C.7.1, if the parameter T (in a call on a
     subprogram of an instance of this package) identifies a nonexistent
     task, the execution of the program is erroneous.



                                   Annex D
                                 (normative)


                              Real-Time Systems



1   {real-time systems} {embedded systems} This Annex specifies additional
characteristics of Ada implementations intended for real-time systems
software.  To conform to this Annex, an implementation shall also conform to
the Systems Programming Annex.


                                   Metrics

2   {metrics} The metrics are documentation requirements; an implementation
shall document the values of the language-defined metrics for at least one
configuration [of hardware or an underlying system] supported by the
implementation, and shall document the details of that configuration.

        2.a   Implementation defined:  Values of all Metrics.

        2.b   Reason:  The actual values of the metrics are likely to depend
        on hardware configuration details that are variable and generally
        outside the control of a compiler vendor.

3   The metrics do not necessarily yield a simple number.  [For some, a range
is more suitable, for others a formula dependent on some parameter is
appropriate, and for others, it may be more suitable to break the metric into
several cases.]  Unless specified otherwise, the metrics in this annex are
expressed in processor clock cycles.  For metrics that require documentation
of an upper bound, if there is no upper bound, the implementation shall
report that the metric is unbounded.

        3.a   Discussion:  There are several good reasons to specify metrics
        in seconds; there are however equally good reasons to specify them in
        processor clock cycles.  In defining the metrics, we have tried to
        strike a balance on a case-by-case basis.

        3.b   It has been suggested that all metrics should be given names,
        so that ``data-sheets'' could be formulated and published by vendors.
        However the paragraph number can serve that purpose.


     NOTES
4    (1) The specification of the metrics makes a distinction between upper
     bounds and simple execution times.  Where something is just specified as
     ``the execution time of'' a piece of code, this leaves one the freedom
     to choose a nonpathological case.  This kind of metric is of the form
     ``there exists a program such that the value of the metric is V''.
     Conversely, the meaning of upper bounds is ``there is no program such
     that the value of the metric is greater than V''.  This kind of metric
     can only be partially tested, by finding the value of V for one or more
     test programs.

5    (2) The metrics do not cover the whole language; they are limited to
     features that are specified in Annex C, ``Systems Programming'' and in
     this Annex.  The metrics are intended to provide guidance to potential
     users as to whether a particular implementation of such a feature is
     going to be adequate for a particular real-time application.  As such,
     the metrics are aimed at known implementation choices that can result in
     significant performance differences.

6    (3) The purpose of the metrics is not necessarily to provide
     fine-grained quantitative results or to serve as a comparison between
     different implementations on the same or different platforms.  Instead,
     their goal is rather qualitative; to define a standard set of
     approximate values that can be measured and used to estimate the general
     suitability of an implementation, or to evaluate the comparative utility
     of certain features of an implementation for a particular real-time
     application.


                            Extensions to Ada 83

        6.a   {extensions to Ada 83} This Annex is new to Ada 9X.



D.1 Task Priorities

1   [This clause specifies the priority model for real-time systems.  In
addition, the methods for specifying priorities are defined.]


                                   Syntax

    2   The form of a pragma Priority is as follows:


3     pragma Priority(expression);

    4   The form of a pragma Interrupt_Priority is as follows:


5     pragma Interrupt_Priority[(expression)];


                            Name Resolution Rules

6   {expected type [Priority pragma argument]} {expected type [Interrupt_
Priority pragma argument]} The expected type for the expression in a Priority
or Interrupt_Priority pragma is Integer.


                               Legality Rules

7   A Priority pragma is allowed only immediately within a task_definition, a
protected_definition, or the declarative_part of a subprogram_body.  An
Interrupt_Priority pragma is allowed only immediately within a task_
definition or a protected_definition.  At most one such pragma shall appear
within a given construct.

8   For a Priority pragma that appears in the declarative_part of a
subprogram_body, the expression shall be static, and its value shall be in
the range of System.Priority.

        8.a   Reason:  This value is needed before it gets elaborated, when
        the environment task starts executing.


                              Static Semantics

9   The following declarations exist in package System:

10  subtype Any_Priority is Integer range implementation-defined;
    subtype Priority is Any_Priority range Any_Priority'First .. implementation\
-defined;
    subtype Interrupt_Priority is Any_Priority range Priority'Last+1 .. Any_Pri\
ority'Last;

11  Default_Priority : constant Priority := (Priority'First + Priority'Last)/2;\
{94-4661.a}

        11.a   Implementation defined:  The declarations of Any_Priority and
        Priority.

12   The full range of priority values supported by an implementation is
specified by the subtype Any_Priority.  The subrange of priority values that
are high enough to require the blocking of one or more interrupts is
specified by the subtype Interrupt_Priority.  [The subrange of priority
values below System.Interrupt_Priority'First is specified by the subtype
System.Priority.]

13   The priority specified by a Priority or Interrupt_Priority pragma is the
value of the expression in the pragma, if any.  If there is no expression in
an Interrupt_Priority pragma, the priority value is Interrupt_Priority'Last.


                              Dynamic Semantics

14   A Priority pragma has no effect if it occurs in the declarative_part of
the subprogram_body of a subprogram other than the main subprogram.

15   {task priority} {priority} {priority inheritance} {base priority}
{active priority} A task priority is an integer value that indicates a degree
of urgency and is the basis for resolving competing demands of tasks for
resources.  Unless otherwise specified, whenever tasks compete for processors
or other implementation-defined resources, the resources are allocated to the
task with the highest priority value.  The base priority of a task is the
priority with which it was created, or to which it was later set by Dynamic_
Priorities.Set_Priority (see D.5).  At all times, a task also has an active
priority, which generally reflects its base priority as well as any priority
it inherits from other sources.  Priority inheritance is the process by which
the priority of a task or other entity (e.g. a protected object; see D.3) is
used in the evaluation of another task's active priority.

        15.a   Implementation defined:  Implementation-defined execution
        resources.

16   The effect of specifying such a pragma in a protected_definition is
discussed in D.3.

17   {creation (of a task object)} The expression in a Priority or Interrupt_
Priority pragma that appears in a task_definition is evaluated for each task
object (see 9.1).  For a Priority pragma, the value of the expression is
converted to the subtype Priority; for an Interrupt_Priority pragma, this
value is converted to the subtype Any_Priority.  The priority value is then
associated with the task object whose task_definition contains the pragma.
{implicit subtype conversion [pragma Priority]} {implicit subtype conversion
[pragma Interrupt_Priority]}

18   Likewise, the priority value is associated with the environment task if
the pragma appears in the declarative_part of the main subprogram.

19   The initial value of a task's base priority is specified by default or
by means of a Priority or Interrupt_Priority pragma.  [After a task is
created, its base priority can be changed only by a call to Dynamic_
Priorities.Set_Priority (see D.5).]  The initial base priority of a task in
the absence of a pragma is the base priority of the task that creates it at
the time of creation (see 9.1).  If a pragma Priority does not apply to the
main subprogram, the initial base priority of the environment task is
System.Default_Priority.  [The task's active priority is used when the task
competes for processors.  Similarly, the task's active priority is used to
determine the task's position in any queue when Priority_Queuing is specified
(see D.4).]

20   At any time, the active priority of a task is the maximum of all the
priorities the task is inheriting at that instant.  For a task that is not
held (see D.11), its base priority is always a source of priority
inheritance.  Other sources of priority inheritance are specified under the
following conditions:

        20.a   Discussion:  Other parts of the annex, e.g.  D.11, define
        other sources of priority inheritance.

   21  During activation, a task being activated inherits the active
       priority of the its activator (see 9.2).

   22  During rendezvous, the task accepting the entry call inherits the
       active priority of the caller (see 9.5.3).

   23  During a protected action on a protected object, a task inherits
       the ceiling priority of the protected object (see 9.5 and D.3).

24   In all of these cases, the priority ceases to be inherited as soon as
the condition calling for the inheritance no longer exists.


                         Implementation Requirements

25   The range of System.Interrupt_Priority shall include at least one value.

26   The range of System.Priority shall include at least 30 values.


     NOTES
27   (4) The priority expression can include references to discriminants of
     the enclosing type.

28   (5) It is a consequence of the active priority rules that at the point
     when a task stops inheriting a priority from another source, its active
     priority is re-evaluated.  This is in addition to other instances
     described in this Annex for such re-evaluation.

29   (6) An implementation may provide a non-standard mode in which tasks
     inherit priorities under conditions other than those specified above.

   29.a   Ramification:  The use of a Priority or Interrupt_Priority pragma
        does not require the package System to be named in a with_clause for
        the enclosing compilation_unit.


                            Extensions to Ada 83

        29.b   {extensions to Ada 83} The priority of a task is per-object
        and not per-type.

        29.c   Priorities need not be static anymore (except for the main
        subprogram).

                         Wording Changes From Ada 83

        29.d   The description of the Priority pragma has been moved to this
        annex.



D.2 Priority Scheduling

1   [This clause describes the rules that determine which task is selected
for execution when more than one task is ready (see 9.2).  The rules have two
parts: the task dispatching model (see D.2.1), and a specific task
dispatching policy (see D.2.2).]



D.2.1 The Task Dispatching Model

1   [The task dispatching model specifies preemptive scheduling, based on
conceptual priority-ordered ready queues.]


                              Dynamic Semantics

2   A task runs (that is, it becomes a running task) only when it is ready
(see 9.2) and the execution resources required by that task are available.
Processors are allocated to tasks based on each task's active priority.

3   It is implementation defined whether, on a multiprocessor, a task that is
waiting for access to a protected object keeps its processor busy.

        3.a   Implementation defined:  Whether, on a multiprocessor, a task
        that is waiting for access to a protected object keeps its processor
        busy.

4   {task dispatching} {dispatching, task} {task dispatching point
[distributed]} {dispatching point [distributed]} Task dispatching is the
process by which one ready task is selected for execution on a processor.
This selection is done at certain points during the execution of a task
called task dispatching points.  A task reaches a task dispatching point
whenever it becomes blocked, and whenever it becomes ready.  In addition, the
completion of an accept_statement (see 9.5.2), and task termination are task
dispatching points for the executing task.  [Other task dispatching points
are defined throughout this Annex.]

        4.a   Ramification:  On multiprocessor systems, more than one task
        can be chosen, at the same time, for execution on more than one
        processor, as explained below.

5   {ready queue} {head (of a queue)} {tail (of a queue)} {ready task} {task
dispatching policy [partial]} {dispatching policy for tasks [partial]} Task
dispatching policies are specified in terms of conceptual ready queues, task
states, and task preemption.  A ready queue is an ordered list of ready
tasks.  The first position in a queue is called the head of the queue, and
the last position is called the tail of the queue.  A task is ready if it is
in a ready queue, or if it is running.  Each processor has one ready queue
for each priority value.  At any instant, each ready queue of a processor
contains exactly the set of tasks of that priority that are ready for
execution on that processor, but are not running on any processor; that is,
those tasks that are ready, are not running on any processor, and can be
executed using that processor and other available resources.  A task can be
on the ready queues of more than one processor.

        5.a   Discussion:  The core language defines a ready task as one that
        is not blocked.  Here we refine this definition and talk about ready
        queues.

6   {running task} Each processor also has one running task, which is the
task currently being executed by that processor.  Whenever a task running on
a processor reaches a task dispatching point, one task is selected to run on
that processor.  The task selected is the one at the head of the highest
priority nonempty ready queue; this task is then removed from all ready
queues to which it belongs.

        6.a   Discussion:  There is always at least one task to run, if we
        count the idle task.

7   {preemptible resource} A preemptible resource is a resource that while
allocated to one task can be allocated (temporarily) to another instead.
Processors are preemptible resources.  Access to a protected object (see
9.5.1) is a nonpreemptible resource.

        7.a   Reason:  A processor that is executing a task is available to
        execute tasks of higher priority, within the set of tasks that that
        processor is able to execute.  Write access to a protected object, on
        the other hand, cannot be granted to a new task before the old task
        has released it.

{preempted task} When a higher-priority task is dispatched to the processor,
and the previously running task is placed on the appropriate ready queue, the
latter task is said to be preempted.

8   {task dispatching point [partial]} {dispatching point [partial]} A new
running task is also selected whenever there is a nonempty ready queue with a
higher priority than the priority of the running task, or when the task
dispatching policy requires a running task to go back to a ready queue.
[These are also task dispatching points.]

        8.a   Ramification:  Thus, when a task becomes ready, this is a task
        dispatching point for all running tasks of lower priority.


                         Implementation Permissions

9   An implementation is allowed to define additional resources as execution
resources, and to define the corresponding allocation policies for them.
Such resources may have an implementation defined effect on task dispatching
(see D.2.2).  {94-4967.a}

        9.a   Implementation defined:  The affect of implementation defined
        execution resources on task dispatching.

10   An implementation may place implementation-defined restrictions on tasks
whose active priority is in the Interrupt_Priority range.

        10.a   Ramification:  For example, on some operating systems, it
        might be necessary to disallow them altogether.  This permission
        applies to tasks whose priority is set to interrupt level for any
        reason: via a pragma, via a call to Dynamic_Priorities.Set_Priority,
        or via priority inheritance.


     NOTES
11   (7) Section 9 specifies under which circumstances a task becomes ready.
     The ready state is affected by the rules for task activation and
     termination, delay statements, and entry calls.  {blocked [partial]}
     When a task is not ready, it is said to be blocked.

12   (8) An example of a possible implementation-defined execution resource
     is a page of physical memory, which needs to be loaded with a particular
     page of virtual memory before a task can continue execution.

13   (9) The ready queues are purely conceptual; there is no requirement that
     such lists physically exist in an implementation.

14   (10) While a task is running, it is not on any ready queue.  Any time
     the task that is running on a processor is added to a ready queue, a new
     running task is selected for that processor.

15   (11) In a multiprocessor system, a task can be on the ready queues of
     more than one processor.  At the extreme, if several processors share
     the same set of ready tasks, the contents of their ready queues is
     identical, and so they can be viewed as sharing one ready queue, and can
     be implemented that way.  [Thus, the dispatching model covers
     multiprocessors where dispatching is implemented using a single ready
     queue, as well as those with separate dispatching domains.]

16   (12) The priority of a task is determined by rules specified in this
     subclause, and under D.1, ``Task Priorities'', D.3, ``Priority Ceiling
     Locking'', and D.5, ``Dynamic Priorities''.



D.2.2 The Standard Task Dispatching Policy

                                   Syntax

    1   The form of a pragma Task_Dispatching_Policy is as follows:


2     pragma Task_Dispatching_Policy(policy_identifier );


                               Legality Rules

3   The policy_identifier shall either be FIFO_Within_Priorities or an
implementation-defined identifier.

        3.a   Implementation defined:  Implementation-defined
        policy_identifiers allowed in a pragma Task_Dispatching_Policy.


                           Post-Compilation Rules

4   {post-compilation rules} {configuration pragma [Task_Dispatching_Policy]}
{pragma, configuration [Task_Dispatching_Policy]} A Task_Dispatching_Policy
pragma is a configuration pragma.

5   If the FIFO_Within_Priorities policy is specified for a partition, then
the Ceiling_Locking policy (see D.3) shall also be specified for the
partition.


                              Dynamic Semantics

6   {task dispatching policy} [A task dispatching policy specifies the
details of task dispatching that are not covered by the basic task
dispatching model.  These rules govern when tasks are inserted into and
deleted from the ready queues, and whether a task is inserted at the head or
the tail of the queue for its active priority.]  The task dispatching policy
is specified by a Task_Dispatching_Policy configuration pragma.  {unspecified
[partial]} If no such pragma appears in any of the program units comprising a
partition, the task dispatching policy for that partition is unspecified.

7   The language defines only one task dispatching policy, FIFO_Within_
Priorities; when this policy is in effect, modifications to the ready queues
occur only as follows:

    8  When a blocked task becomes ready, it is added at the tail of the
       ready queue for its active priority.

    9  When the active priority of a ready task that is not running
       changes, or the setting of its base priority takes effect, the
       task is removed from the ready queue for its old active priority
       and is added at the tail of the ready queue for its new active
       priority, except in the case where the active priority is lowered
       due to the loss of inherited priority, in which case the task is
       added at the head of the ready queue for its new active priority.

   10  When the setting of the base priority of a running task takes
       effect, the task is added to the tail of the ready queue for its
       active priority.

   11  When a task executes a delay_statement that does not result in
       blocking, it is added to the tail of the ready queue for its
       active priority.

 11.a   Ramification:  If the delay does result in blocking, the task
        moves to the ``delay queue'', not to the ready queue.

12   {task dispatching point [partial]} {dispatching point [partial]} Each of
the events specified above is a task dispatching point (see D.2.1).

13   In addition, when a task is preempted, it is added at the head of the
ready queue for its active priority.


                         Documentation Requirements

14   {documentation requirements} {priority inversion} Priority inversion is
the duration for which a task remains at the head of the highest priority
ready queue while the processor executes a lower priority task.  The
implementation shall document:

   15  The maximum priority inversion a user task can experience due to
       activity of the implementation (on behalf of lower priority
       tasks), and

   16  whether execution of a task can be preempted by the
       implementation processing of delay expirations for lower priority
       tasks, and if so, for how long.

 16.a   Implementation defined:  Implementation-defined aspects of
        priority inversion.


                         Implementation Permissions

17   Implementations are allowed to define other task dispatching policies,
but need not support more than one such policy per partition.

18   [For optimization purposes,] an implementation may alter the points at
which task dispatching occurs, in an implementation defined manner.  However,
a delay_statement always corresponds to at least one task dispatching point.
{94-4967.a}

        18.a   Implementation defined:  Implementation defined task
        dispatching.


     NOTES
19   (13) If the active priority of a running task is lowered due to loss of
     inherited priority (as it is on completion of a protected operation) and
     there is a ready task of the same active priority that is not running,
     the running task continues to run (provided that there is no higher
     priority task).

20   (14) The setting of a task's base priority as a result of a call to Set_
     Priority does not always take effect immediately when Set_Priority is
     called.  The effect of setting the task's base priority is deferred
     while the affected task performs a protected action.

21   (15) Setting the base priority of a ready task causes the task to move
     to the end of the queue for its active priority, regardless of whether
     the active priority of the task actually changes.



D.3 Priority Ceiling Locking

1   [This clause specifies the interactions between priority task scheduling
and protected object ceilings.  This interaction is based on the concept of
the ceiling priority of a protected object.]


                                   Syntax

    2   The form of a pragma Locking_Policy is as follows:


3     pragma Locking_Policy(policy_identifier);
                               Legality Rules

4   The policy_identifier shall either be Ceiling_Locking or an
implementation-defined identifier.

        4.a   Implementation defined:  Implementation-defined
        policy_identifiers allowed in a pragma Locking_Policy.


                           Post-Compilation Rules

5   {post-compilation rules} {configuration pragma [Locking_Policy]} {pragma,
configuration [Locking_Policy]} A Locking_Policy pragma is a configuration
pragma.


                              Dynamic Semantics

6   {locking policy} [A locking policy specifies the details of protected
object locking.  These rules specify whether or not protected objects have
priorities, and the relationships between these priorities and task
priorities.  In addition, the policy specifies the state of a task when it
executes a protected action, and how its active priority is affected by the
locking.]  The locking policy is specified by a Locking_Policy pragma.  For
implementation-defined locking policies, the effect of a Priority or
Interrupt_Priority pragma on a protected object is implementation defined.
If no Locking_Policy pragma appears in any of the program units comprising a
partition, the locking policy for that partition, as well as the effect of
specifying either a Priority or Interrupt_Priority pragma for a protected
object, are implementation defined.

7   There is one predefined locking policy, Ceiling_Locking; this policy is
defined as follows:

    8  {ceiling priority (of a protected object)} Every protected object
       has a ceiling priority, which is determined by either a Priority
       or Interrupt_Priority pragma as defined in D.1.  The ceiling
       priority of a protected object (or ceiling, for short) is an
       upper bound on the active priority a task can have when it calls
       protected operations of that protected object.

    9  The expression of a Priority or Interrupt_Priority pragma is
       evaluated as part of the creation of the corresponding protected
       object and converted to the subtype System.Any_Priority or
       System.Interrupt_Priority, respectively.  The value of the
       expression is the ceiling priority of the corresponding protected
       object.  {implicit subtype conversion [pragma Priority]}
       {implicit subtype conversion [pragma Interrupt_Priority]}

   10  If an Interrupt_Handler or Attach_Handler pragma (see C.3.1)
       appears in a protected_definition without an Interrupt_Priority
       pragma, the ceiling priority of protected objects of that type is
       implementation defined, but in the range of the subtype
       System.Interrupt_Priority.

 10.a   Implementation defined:  Default ceiling priorities.

   11  If no pragma Priority, Interrupt_Priority, Interrupt_Handler, or
       Attach_Handler is specified in the protected_definition, then the
       ceiling priority of the corresponding protected object is
       System.Priority'Last.

   12  While a task executes a protected action, it inherits the ceiling
       priority of the corresponding protected object.

   13  {Ceiling_Check [partial]} {check, language-defined (Ceiling_
       Check)} {Program_Error (raised by failure of run-time check)}
       When a task calls a protected operation, a check is made that its
       active priority is not higher than the ceiling of the
       corresponding protected object; Program_Error is raised if this
       check fails.


                         Implementation Permissions

14   The implementation is allowed to round all ceilings in a certain
subrange of System.Priority or System.Interrupt_Priority up to the top of
that subrange, uniformly.

        14.a   Discussion:  For example, an implementation might use
        Priority'Last for all ceilings in Priority, and Interrupt_
        Priority'Last for all ceilings in Interrupt_Priority.  This would be
        equivalent to having two ceiling priorities for protected objects,
        ``nonpreemptible'' and ``noninterruptible'', and is an allowed
        behavior.

        14.b   Note that the implementation cannot choose a subrange that
        crosses the boundary between normal and interrupt priorities.

15   Implementations are allowed to define other locking policies, but need
not support more than one such policy per partition.

16   [Since implementations are allowed to place restrictions on code that
runs at an interrupt-level active priority (see C.3.1 and D.2.1), the
implementation may implement a language feature in terms of a protected
object with an implementation-defined ceiling, but the ceiling shall be no
less than Priority'Last.]

        16.a   Implementation defined:  The ceiling of any protected object
        used internally by the implementation.

        16.b   Proof:  This permission follows from the fact that the
        implementation can place restrictions on interrupt handlers and on
        any other code that runs at an interrupt-level active priority.

        16.c   The implementation might protect a storage pool with a
        protected object whose ceiling is Priority'Last, which would cause
        allocators to fail when evaluated at interrupt priority.  Note that
        the ceiling of such an object has to be at least Priority'Last, since
        there is no permission for allocators to fail when evaluated at a
        non-interrupt priority.


                            Implementation Advice

17   The implementation should use names that end with ``_Locking'' for
implementation-defined locking policies.


     NOTES
18   (16) While a task executes in a protected action, it can be preempted
     only by tasks whose active priorities are higher than the ceiling
     priority of the protected object.

19   (17) If a protected object has a ceiling priority in the range of
     Interrupt_Priority, certain interrupts are blocked while protected
     actions of that object execute.  In the extreme, if the ceiling is
     Interrupt_Priority'Last, all blockable interrupts are blocked during
     that time.

20   (18) The ceiling priority of a protected object has to be in the
     Interrupt_Priority range if one of its procedures is to be used as an
     interrupt handler (see C.3).

21   (19) When specifying the ceiling of a protected object, one should
     choose a value that is at least as high as the highest active priority
     at which tasks can be executing when they call protected operations of
     that object.  In determining this value the following factors, which can
     affect active priority, should be considered: the effect of Set_
     Priority, nested protected operations, entry calls, task activation, and
     other implementation-defined factors.

22   (20) Attaching a protected procedure whose ceiling is below the
     interrupt hardware priority to an interrupt causes the execution of the
     program to be erroneous (see C.3.1).

23   (21) On a single processor implementation, the ceiling priority rules
     guarantee that there is no possibility of deadlock involving only
     protected subprograms (excluding the case where a protected operation
     calls another protected operation on the same protected object).



D.4 Entry Queuing Policies

1   [{queuing policy} This clause specifies a mechanism for a user to choose
an entry queuing policy.  It also defines one such policy.  Other policies
are implementation defined.]

        1.a   Implementation defined:  Implementation-defined queuing
        policies.


                                   Syntax

    2   The form of a pragma Queuing_Policy is as follows:


3     pragma Queuing_Policy(policy_identifier);


                               Legality Rules

4   The policy_identifier shall be either FIFO_Queuing, Priority_Queuing or
an implementation-defined identifier.


                           Post-Compilation Rules

5   {post-compilation rules} {configuration pragma [Queuing_Policy]} {pragma,
configuration [Queuing_Policy]} A Queuing_Policy pragma is a configuration
pragma.


                              Dynamic Semantics

6   {queuing policy} [A queuing policy governs the order in which tasks are
queued for entry service, and the order in which different entry queues are
considered for service.]  The queuing policy is specified by a Queuing_Policy
pragma.

        6.a   Ramification:  The queuing policy includes entry queuing order,
        the choice among open alternatives of a selective_accept, and the
        choice among queued entry calls of a protected object when more than
        one entry_barrier condition is True.

7   Two queuing policies, FIFO_Queuing and Priority_Queuing, are language
defined.  If no Queuing_Policy pragma appears in any of the program units
comprising the partition, the queuing policy for that partition is FIFO_
Queuing.  The rules for this policy are specified in 9.5.3 and 9.7.1.

8   The Priority_Queuing policy is defined as follows:

    9  {priority of an entry call} The calls to an entry [(including a
       member of an entry family)] are queued in an order consistent
       with the priorities of the calls.  The priority of an entry call
       is initialized from the active priority of the calling task at
       the time the call is made, but can change later.  Within the same
       priority, the order is consistent with the calling (or requeuing,
       or priority setting) time (that is, a FIFO order).

   10  After a call is first queued, changes to the active priority of a
       task do not affect the priority of the call, unless the base
       priority of the task is set.

   11  When the base priority of a task is set (see D.5), if the task is
       blocked on an entry call, and the call is queued, the priority of
       the call is updated to the new active priority of the calling
       task.  This causes the call to be removed from and then
       reinserted in the queue at the new active priority.

 11.a   Reason:  A task is blocked on an entry call if the entry call is
        simple, conditional, or timed.  If the call came from the
        triggering_statement of an asynchronous_select, or a requeue
        thereof, then the task is not blocked on that call; such calls
        do not have their priority updated.  Thus, there can exist many
        queued calls from a given task (caused by many nested ATC's),
        but a task can be blocked on only one call at a time.

 11.b   A previous version of Ada 9X required queue reordering in the
        asynchronous_select case as well.  If the call corresponds to a
        ``synchronous'' entry call, then the task is blocked while
        queued, and it makes good sense to move it up in the queue if
        its priority is raised.

 11.c   However, if the entry call is ``asynchronous,'' that is, it is
        due to an asynchronous_select whose triggering_statement is an
        entry call, then the task is not waiting for this entry call, so
        the placement of the entry call on the queue is irrelevant to
        the rate at which the task proceeds.

 11.d   Furthermore, when an entry is used for asynchronous_selects, it
        is almost certain to be a ``broadcast'' entry or have only one
        caller at a time.  For example, if the entry is used to notify
        tasks of a mode switch, then all tasks on the entry queue would
        be signaled when the mode changes.  Similarly, if it is
        indicating some interrupting event such as a control-C, all
        tasks sensitive to the interrupt will want to be informed that
        the event occurred.  Hence, the order on such a queue is
        essentially irrelevant.

 11.e   Given the above, it seems an unnecessary semantic and
        implementation complexity to specify that asynchronous queued
        calls are moved in response to dynamic priority changes.
        Furthermore, it is somewhat inconsistent, since the call was
        originally queued based on the active priority of the task, but
        dynamic priority changes are changing the base priority of the
        task, and only indirectly the active priority.  We say
        explicitly that asynchronous queued calls are not affected by
        normal changes in active priority during the execution of an
        abortable_part.  Saying that, if a change in the base priority
        affects the active priority, then we do want the calls
        reordered, would be inconsistent.  It would also require the
        implementation to maintain a readily accessible list of all
        queued calls which would not otherwise be necessary.

 11.f   Several rules were removed or simplified when we changed the
        rules so that calls due to asynchronous_selects are never moved
        due to intervening changes in active priority, be they due to
        protected actions, some other priority inheritance, or changes
        in the base priority.

   12  When more than one condition of an entry_barrier of a protected
       object becomes True, and more than one of the respective queues
       is nonempty, the call with the highest priority is selected.  If
       more than one such call has the same priority, the call that is
       queued on the entry whose declaration is first in textual order
       in the protected_definition is selected.  For members of the same
       entry family, the one with the lower family index is selected.

   13  If the expiration time of two or more open delay_alternatives is
       the same and no other accept_alternatives are open, the
       sequence_of_statements of the delay_alternative that is first in
       textual order in the selective_accept is executed.

   14  When more than one alternative of a selective_accept is open and
       has queued calls, an alternative whose queue has the
       highest-priority call at its head is selected.  If two or more
       open alternatives have equal-priority queued calls, then a call
       on the entry in the accept_alternative that is first in textual
       order in the selective_accept is selected.


                         Implementation Permissions

15   Implementations are allowed to define other queuing policies, but need
not support more than one such policy per partition.


                            Implementation Advice

16   The implementation should use names that end with ``_Queuing'' for
implementation-defined queuing policies.



D.5 Dynamic Priorities

1   [This clause specifies how the base priority of a task can be modified or
queried at run time.]


                              Static Semantics

2   The following language-defined library package exists:

3   with System;
    with Ada.Task_Identification; -- See C.7.1
    package Ada.Dynamic_Priorities is

4       procedure Set_Priority(Priority : in System.Any_Priority;
                                            T : in Ada.Task_Identification.Task\
_ID :=
                                            Ada.Task_Identification.Current_Tas\
k);

5       function Get_Priority (T : Ada.Task_Identification.Task_ID :=
                                            Ada.Task_Identification.Current_Tas\
k)
                                            return System.Any_Priority;

6   end Ada.Dynamic_Priorities;


                              Dynamic Semantics

7   The procedure Set_Priority sets the base priority of the specified task
to the specified Priority value.  Set_Priority has no effect if the task is
terminated.

8   The function Get_Priority returns T's current base priority.  {Tasking_
Error (raised by failure of run-time check)} Tasking_Error is raised if the
task is terminated.

        8.a   Reason:  There is no harm in setting the priority of a
        terminated task.  A previous version of Ada 9X made this a run-time
        error.  However, there is little difference between setting the
        priority of a terminated task, and setting the priority of a task
        that is about to terminate very soon; neither case should be an
        error.  Furthermore, the run-time check is not necessarily feasible
        to implement on all systems, since priority changes might be deferred
        due to inter-processor communication overhead, so the error might not
        be detected until after Set_Priority has returned.

        8.b   However, we wish to allow implementations to avoid storing
        ``extra'' information about terminated tasks.  Therefore, we make
        Get_Priority of a terminated task raise an exception; the
        implementation need not continue to store the priority of a task that
        has terminated.

9   {Program_Error (raised by failure of run-time check)} Program_Error is
raised by Set_Priority and Get_Priority if T is equal to Null_Task_ID.

10   Setting the task's base priority to the new value takes place as soon as
is practical but not while the task is performing a protected action.  This
setting occurs no later then the next abort completion point of the task T
(see 9.8).

        10.a   Implementation Note:  When Set_Priority is called by a task T1
        to set the priority of T2, if T2 is blocked, waiting on an entry call
        queued on a protected object, the entry queue needs to be reordered.
        Since T1 might have a priority that is higher than the ceiling of the
        protected object, T1 cannot, in general, do the reordering.  One way
        to implement this is to wake T2 up and have T2 do the work.  This is
        similar to the disentangling of queues that needs to happen when a
        high-priority task aborts a lower-priority task, which might have a
        call queued on a protected object with a low ceiling.

        10.b   Reason:  A previous version of Ada 9X made it a run-time error
        for a high-priority task to set the priority of a lower-priority task
        that has a queued call on a protected object with a low ceiling.
        This was changed because:

         10.c  The check was not feasible to implement on all systems,
               since priority changes might be deferred due to
               inter-processor communication overhead.  The calling task
               would continue to execute without finding out whether the
               operation succeeded or not.

         10.d  The run-time check would tend to cause intermittent
               system failures -- how is the caller supposed to know
               whether the other task happens to have a queued call at
               any given time?  Consider for example an interrupt that
               needs to trigger a priority change in some task.  The
               interrupt handler could not safely call Set_Priority
               without knowing exactly what the other task is doing, or
               without severely restricting the ceilings used in the
               system.  If the interrupt handler wants to hand the job
               off to a third task whose job is to call Set_Priority,
               this won't help, because one would normally want the
               third task to have high priority.
                          Bounded (Run-Time) Errors

11   {bounded error} If a task is blocked on a protected entry call, and the
call is queued, it is a bounded error to raise its base priority above the
ceiling priority of the corresponding protected object.  {94-4768.t} When an
entry call is cancelled, it is a bounded error if the priority of the calling
task is higher than the ceiling priority of the corresponding protected
object.  {Program_Error (raised by failure of run-time check)} In either of
these cases, either Program_Error is raised in the task that called the
entry, or its priority is temporarily lowered, or both, or neither.

        11.a   Ramification:  Note that the error is ``blamed'' on the task
        that did the entry call, not the task that called Set_Priority.  This
        seems to make sense for the case of a task blocked on a call, since
        if the Set_Priority had happened a little bit sooner, before the task
        queued a call, the entry-calling task would get the error.  In the
        other case, there is no reason not to raise the priority of a task
        that is executing in an abortable_part, so long as its priority is
        lowered before it gets to the end and needs to cancel the call.  The
        priority might need to be lowered to allow it to remove the call from
        the entry queue, in order to avoid violating the ceiling.  This seems
        relatively harmless, since there is an error, and the task is about
        to start raising an exception anyway.


                             Erroneous Execution

12   {erroneous execution} If any subprogram in this package is called with a
parameter T that specifies a task object that no longer exists, the execution
of the program is erroneous.

        12.a   Ramification:  Note that this rule overrides the above rule
        saying that Program_Error is raised on Get_Priority of a terminated
        task.  If the task object still exists, and the task is terminated,
        Get_Priority raises Program_Error.  However, if the task object no
        longer exists, calling Get_Priority causes erroneous execution.


                                   Metrics

13   {metrics} The implementation shall document the following metric:

   14  The execution time of a call to Set_Priority, for the
       nonpreempting case, in processor clock cycles.  This is measured
       for a call that modifies the priority of a ready task that is not
       running (which cannot be the calling one), where the new base
       priority of the affected task is lower than the active priority
       of the calling task, and the affected task is not on any entry
       queue and is not executing a protected operation.


     NOTES
15   (22) Setting a task's base priority affects task dispatching.  First, it
     can change the task's active priority.  Second, under the standard task
     dispatching policy it always causes the task to move to the tail of the
     ready queue corresponding to its active priority, even if the new base
     priority is unchanged.

16   (23) Under the priority queuing policy, setting a task's base priority
     has an effect on a queued entry call if the task is blocked waiting for
     the call.  That is, setting the base priority of a task causes the
     priority of a queued entry call from that task to be updated and the
     call to be removed and then reinserted in the entry queue at the new
     priority (see D.4), unless the call originated from the triggering_
     statement of an asynchronous_select.

17   (24) The effect of two or more Set_Priority calls executed in parallel
     on the same task is defined as executing these calls in some serial
     order.  {94-4761.u}

   17.a   Proof:  This follows from the general reentrancy requirements
        stated near the beginning of Annex A, ``Predefined Language
        Environment''.

18   (25) The rule for when Tasking_Error is raised for Set_Priority or Get_
     Priority is different from the rule for when Tasking_Error is raised on
     an entry call (see 9.5.3).  In particular, setting or querying the
     priority of a completed or an abnormal task is allowed, so long as the
     task is not yet terminated.

19   (26) Changing the priorities of a set of tasks can be performed by a
     series of calls to Set_Priority for each task separately.  For this to
     work reliably, it should be done within a protected operation that has
     high enough ceiling priority to guarantee that the operation completes
     without being preempted by any of the affected tasks.



D.6 Preemptive Abort

1   [This clause specifies requirements on the immediacy with which an
aborted construct is completed.]


                              Dynamic Semantics

2   On a system with a single processor, an aborted construct is completed
immediately at the first point that is outside the execution of an
abort-deferred operation.


                         Documentation Requirements

3   {documentation requirements} On a multiprocessor, the implementation
shall document any conditions that cause the completion of an aborted
construct to be delayed later than what is specified for a single processor.

        3.a   Implementation defined:  On a multiprocessor, any conditions
        that cause the completion of an aborted construct to be delayed later
        than what is specified for a single processor.


                                   Metrics

4   {metrics} The implementation shall document the following metrics:

    5  The execution time, in processor clock cycles, that it takes for
       an abort_statement to cause the completion of the aborted task.
       This is measured in a situation where a task T2 preempts task T1
       and aborts T1.  T1 does not have any finalization code.  T2 shall
       verify that T1 has terminated, by means of the Terminated
       attribute.

    6  On a multiprocessor, an upper bound in seconds, on the time that
       the completion of an aborted task can be delayed beyond the point
       that it is required for a single processor.

    7  An upper bound on the execution time of an asynchronous_select,
       in processor clock cycles.  This is measured between a point
       immediately before a task T1 executes a protected operation
       Pr.Set that makes the condition of an entry_barrier Pr.Wait true,
       and the point where task T2 resumes execution immediately after
       an entry call to Pr.Wait in an asynchronous_select.  T1 preempts
       T2 while T2 is executing the abortable part, and then blocks
       itself so that T2 can execute.  The execution time of T1 is
       measured separately, and subtracted.

    8  An upper bound on the execution time of an asynchronous_select,
       in the case that no asynchronous transfer of control takes place.
       This is measured between a point immediately before a task
       executes the asynchronous_select with a nonnull abortable part,
       and the point where the task continues execution immediately
       after it.  The execution time of the abortable part is
       subtracted.


                            Implementation Advice

9   Even though the abort_statement is included in the list of potentially
blocking operations (see 9.5.1), it is recommended that this statement be
implemented in a way that never requires the task executing the abort_
statement to block.

10   On a multi-processor, the delay associated with aborting a task on
another processor should be bounded; the implementation should use periodic
polling, if necessary, to achieve this.


     NOTES
11   (27) Abortion does not change the active or base priority of the aborted
     task.

12   (28) Abortion cannot be more immediate than is allowed by the rules for
     deferral of abortion during finalization and in protected actions.



D.7 Tasking Restrictions

1   [This clause defines restrictions that can be used with a pragma
Restrictions (see 13.12) to facilitate the construction of highly efficient
tasking run-time systems.]


                              Static Semantics

2   The following restriction_identifiers are language defined:

3   {Restrictions (No_Task_Hierarchy)} No_Task_Hierarchy
                All (nonenvironment) tasks depend directly on the environment
                task of the partition.

4   {Restrictions (No_Nested_Finalization)} No_Nested_Finaliza-
                tion
                Objects with controlled parts and access types that designate
                such objects shall be declared only at library level.

4.a     Ramification:  Note that protected types with entries and
        interrupt-handling protected types have nontrivial finalization
        actions.  However, this restriction does not restrict those things.

5   {Restrictions (No_Abort_Statements)} No_Abort_Statements
                There are no abort_statements, and there are no calls on
                Task_Identification.Abort_Task.

6   {Restrictions (No_Terminate_Alternatives)} No_Terminate_Al-
                ternatives
                There are no selective_accepts with terminate_alternatives.

7   {Restrictions (No_Task_Allocators)} No_Task_Allocators
                There are no allocators for task types or types containing
                task subcomponents.

8   {Restrictions (No_Implicit_Heap_Allocations)} No_Implicit_
                Heap_Allocations
                There are no operations that implicitly require heap storage
                allocation to be performed by the implementation.  The
                operations that implicitly require heap storage allocation
                are implementation defined.

8.a     Implementation defined:  Any operations that implicitly require heap
        storage allocation.

9   No_Dynamic_Priorities
                There are no semantic dependences on the package Dynamic_
                Priorities.  {Restrictions (No_Dynamic_Priorities)}

10  {Restrictions (No_Asynchronous_Control)} No_Asynchronous_
                Control
                There are no semantic dependences on the package
                Asynchronous_Task_Control.

11   The following restriction_parameter_identifiers are language defined:

12  {Restrictions (Max_Select_Alternatives)} Max_Select_Alter-
                natives
                Specifies the maximum number of alternatives in a selective_
                accept.

13  {Restrictions (Max_Task_Entries)} Max_Task_Entries
                Specifies the maximum number of entries per task.  The bounds
                of every entry family of a task unit shall be static, or
                shall be defined by a discriminant of a subtype whose
                corresponding bound is static.  [A value of zero indicates
                that no rendezvous are possible.]

14  Max_Protected_Entries
                Specifies the maximum number of entries per protected type.
                The bounds of every entry family of a protected unit shall be
                static, or shall be defined by a discriminant of a subtype
                whose corresponding bound is static.  {Restrictions (Max_
                Protected_Entries)}


                              Dynamic Semantics

15   If the following restrictions are violated, the behavior is
implementation defined.  {Storage_Check [partial]} {check, language-defined
(Storage_Check)} {Storage_Error (raised by failure of run-time check)} If an
implementation chooses to detect such a violation, Storage_Error should be
raised.

16   The following restriction_parameter_identifiers are language defined:

17  {Restrictions (Max_Storage_At_Blocking)} Max_Storage_At_
                Blocking
                Specifies the maximum portion [(in storage elements)] of a
                task's Storage_Size that can be retained by a blocked task.

18  {Restrictions (Max_Asynchronous_Select_Nesting)} Max_
                Asynchronous_Select_Nesting
                Specifies the maximum dynamic nesting level of asynchronous_
                selects.  [A value of zero prevents the use of any
                asynchronous_select.]  {94-4567.a}

19  {Restrictions (Max_Tasks)} Max_Tasks
                Specifies the maximum number of task creations that may be
                executed over the lifetime of a partition, not counting the
                creation of the environment task.

19.a    Ramification:  Note that this is not a limit on the number of tasks
        active at a given time; it is a limit on the total number of task
        creations that occur.

19.b    Implementation Note:  We envision an implementation approach that
        places TCBs or pointers to them in a fixed-size table, and never
        reuses table elements.

20   It is implementation defined whether the use of pragma Restrictions
results in a reduction in executable program size, storage requirements, or
execution time.  If possible, the implementation should provide quantitative
descriptions of such effects for each restriction.

        20.a   Implementation defined:  Implementation-defined aspects of
        pragma Restrictions.


                            Implementation Advice

21   When feasible, the implementation should take advantage of the specified
restrictions to produce a more efficient implementation.


     NOTES
22   (29) The above Storage_Checks can be suppressed with pragma Suppress.



D.8 Monotonic Time

1   [This clause specifies a high-resolution, monotonic clock package.]


                              Static Semantics

2   The following language-defined library package exists:

3   package Ada.Real_Time is

4     type Time is private;
      Time_First : constant Time;
      Time_Last : constant Time;
      Time_Unit : constant := implementation-defined-real-number;

5


6     type Time_Span is private;
      Time_Span_First : constant Time_Span;
      Time_Span_Last : constant Time_Span;
      Time_Span_Zero : constant Time_Span;
      Time_Span_Unit : constant Time_Span;

7

      Tick : constant Time_Span;
      function Clock return Time;

8

      function "+" (Left : Time; Right : Time_Span) return Time;
      function "+" (Left : Time_Span; Right : Time) return Time;
      function "-" (Left : Time; Right : Time_Span) return Time;
      function "-" (Left : Time; Right : Time) return Time_Span;

9

      function "<" (Left, Right : Time) return Boolean;
      function "<="(Left, Right : Time) return Boolean;
      function ">" (Left, Right : Time) return Boolean;
      function ">="(Left, Right : Time) return Boolean;

10

      function "+" (Left, Right : Time_Span) return Time_Span;
      function "-" (Left, Right : Time_Span) return Time_Span;
      function "-" (Right : Time_Span) return Time_Span;
      function "*" (Left : Time_Span; Right : Integer) return Time_Span;
      function "*" (Left : Integer; Right : Time_Span) return Time_Span;
      function "/" (Left, Right : Time_Span) return Integer;
      function "/" (Left : Time_Span; Right : Integer) return Time_Span;

11    function "abs"(Right : Time_Span) return Time_Span;

12

      function "<" (Left, Right : Time_Span) return Boolean;
      function "<="(Left, Right : Time_Span) return Boolean;
      function ">" (Left, Right : Time_Span) return Boolean;
      function ">="(Left, Right : Time_Span) return Boolean;

13

      function To_Duration (TS : Time_Span) return Duration;
      function To_Time_Span (D : Duration) return Time_Span;

14

      function Nanoseconds  (NS : Integer) return Time_Span;
      function Microseconds (US : Integer) return Time_Span;
      function Milliseconds (MS : Integer) return Time_Span;

15    type Seconds_Count is range implementation-defined;

16    procedure Split(T : in Time; SC : out Seconds_Count; TS : out Time_Span);
      function Time_Of(SC : Seconds_Count; TS : Time_Span) return Time;

17  private
       ... -- not specified by the language
    end Ada.Real_Time;

        17.a   Implementation defined:  Implementation-defined aspects of
        package Real_Time.

18   {real time} In this Annex, real time is defined to be the physical time
as observed in the external environment.  The type Time is a time type as
defined by 9.6; [values of this type may be used in a delay_until_statement.]
Values of this type represent segments of an ideal time line.  The set of
values of the type Time corresponds one-to-one with an implementation-defined
range of mathematical integers.

        18.a   Discussion:  Informally, real time is defined to be the
        International Atomic Time (TAI) which is monotonic and nondecreasing.
        We use it here for the purpose of discussing rate of change and
        monotonic behavior only.  It does not imply anything about the
        absolute value of Real_Time.Clock, or about Real_Time.Time being
        synchronized with TAI.  It is also used for real time in the metrics,
        for comparison purposes.
        18.b   Implementation Note:  The specification of TAI as ``real
        time'' does not preclude the use of a simulated TAI clock for
        simulated execution environments.

19   {epoch} {unspecified [partial]} The Time value I represents the
half-open real time interval that starts with E+I*Time_Unit and is limited by
E+(I+1)*Time_Unit, where Time_Unit is an implementation-defined real number
and E is an unspecified origin point, the epoch, that is the same for all
values of the type Time.  It is not specified by the language whether the
time values are synchronized with any standard time reference.  [For example,
E can correspond to the time of system initialization or it can correspond to
the epoch of some time standard.]

        19.a   Discussion:  E itself does not have to be a proper time value.

        19.b   This half-open interval I consists of all real numbers R such
        that E+I*Time_Unit <= R < E+(I+1)*Time_Unit.

20   Values of the type Time_Span represent length of real time duration.
The set of values of this type corresponds one-to-one with an
implementation-defined range of mathematical integers.  The Time_Span value
corresponding to the integer I represents the real-time duration I*Time_Unit.

        20.a   Reason:  The purpose of this type is similar to
        Standard.Duration; the idea is to have a type with a higher
        resolution.

        20.b   Discussion:  We looked at many possible names for this type:
        Real_Time.Duration, Fine_Duration, Interval, Time_Interval_Length,
        Time_Measure, and more.  Each of these names had some problems, and
        we've finally settled for Time_Span.

21   Time_First and Time_Last are the smallest and largest values of the Time
type, respectively.  Similarly, Time_Span_First and Time_Span_Last are the
smallest and largest values of the Time_Span type, respectively.

22   A value of type Seconds_Count represents an elapsed time, measured in
seconds, since the epoch.


                              Dynamic Semantics

23   Time_Unit is the smallest amount of real time representable by the Time
type; it is expressed in seconds.  Time_Span_Unit is the difference between
two successive values of the Time type.  It is also the smallest positive
value of type Time_Span.  Time_Unit and Time_Span_Unit represent the same
real time duration.  {clock tick} A clock tick is a real time interval during
which the clock value (as observed by calling the Clock function) remains
constant.  Tick is the average length of such intervals.

24   The function To_Duration converts the value TS to a value of type
Duration.  Similarly, the function To_Time_Span converts the value D to a
value of type Time_Span.  For both operations, the result is rounded to the
nearest exactly representable value (away from zero if exactly halfway
between two exactly representable values).

25   To_Duration(Time_Span_Zero) returns 0.0, and To_Time_Span(0.0) returns
Time_Span_Zero.

26   The functions Nanoseconds, Microseconds, and Milliseconds convert the
input parameter to a value of the type Time_Span.  NS, US, and MS are
interpreted as a number of nanoseconds, microseconds, and milliseconds
respectively.  The result is rounded to the nearest exactly representable
value (away from zero if exactly halfway between two exactly representable
values).

        26.a   Discussion:  The above does not imply that the Time_Span type
        will have to accommodate Integer'Last of milliseconds; Constraint_
        Error is allowed to be raised.

27   The effects of the operators on Time and Time_Span are as for the
operators defined for integer types.

        27.a   Implementation Note:  Though time values are modeled by
        integers, the types Time and Time_Span need not be implemented as
        integers.

28   The function Clock returns the amount of time since the epoch.

29   The effects of the Split and Time_Of operations are defined as follows,
treating values of type Time, Time_Span, and Seconds_Count as mathematical
integers.  The effect of Split(T,SC,TS) is to set SC and TS to values such
that T*Time_Unit = SC*1.0 + TS*Time_Unit, and 0.0 <= TS*Time_Unit < 1.0.  The
value returned by Time_Of(SC,TS) is the value T such that T*Time_Unit =
SC*1.0 + TS*Time_Unit.


                         Implementation Requirements

30   The range of Time values shall be sufficient to uniquely represent the
range of real times from program start-up to 50 years later.  Tick shall be
no greater than 1 millisecond.  Time_Unit shall be less than or equal to 20
microseconds.

        30.a   Implementation Note:  The required range and accuracy of Time
        are such that 32-bits worth of seconds and 32-bits worth of ticks in
        a second could be used as the representation.

31   Time_Span_First shall be no greater than -3600 seconds, and Time_Span_
Last shall be no less than 3600 seconds.

        31.a   Reason:  This is equivalent to +/- one hour and there is still
        room for a two-microsecond resolution.

32   {clock jump} A clock jump is the difference between two successive
distinct values of the clock (as observed by calling the Clock function).
There shall be no backward clock jumps.


                         Documentation Requirements

33   {documentation requirements} The implementation shall document the
values of Time_First, Time_Last, Time_Span_First, Time_Span_Last, Time_Span_
Unit, and Tick.

34   The implementation shall document the properties of the underlying time
base used for the clock and for type Time, such as the range of values
supported and any relevant aspects of the underlying hardware or operating
system facilities used.

        34.a   Discussion:  If there is an underlying operating system, this
        might include information about which system call is used to
        implement the clock.  Otherwise, it might include information about
        which hardware clock is used.

35   The implementation shall document whether or not there is any
synchronization with external time references, and if such synchronization
exists, the sources of synchronization information, the frequency of
synchronization, and the synchronization method applied.

36   The implementation shall document any aspects of the the external
environment that could interfere with the clock behavior as defined in this
clause.

        36.a   Discussion:  For example, the implementation is allowed to
        rely on the time services of an underlying operating system, and this
        operating system clock can implement time zones or allow the clock to
        be reset by an operator.  This dependence has to be documented.


                                   Metrics

37   {metrics} For the purpose of the metrics defined in this clause, real
time is defined to be the International Atomic Time (TAI).

38   The implementation shall document the following metrics:

   39  An upper bound on the real-time duration of a clock tick.  This
       is a value D such that if t1 and t2 are any real times such that
       t1 < t2 and Clock   = Clock   then t2 - t1 <= D.
                        t1        t2
   40  An upper bound on the size of a clock jump.

   41  {drift rate} An upper bound on the drift rate of Clock with
       respect to real time.  This is a real number D such that

42         E*(1-D) <= (Clock    - Clock ) <= E*(1+D)
                                          t+E        t
                   provided that: Clock  + E*(1+D) <= Time_Last.
                                       t
   43  where Clock  is the value of Clock at time t, and E is a real
                  t
       time duration not less than 24 hours.  The value of E used for
       this metric shall be reported.

 43.a   Reason:  This metric is intended to provide a measurement of the
        long term (cumulative) deviation; therefore, 24 hours is the
        lower bound on the measurement period.  On some implementations,
        this is also the maximum period, since the language does not
        require that the range of the type Duration be more than 24
        hours.  On those implementations that support longer-range
        Duration, longer measurements should be performed.

   44  An upper bound on the execution time of a call to the Clock
       function, in processor clock cycles.

   45  Upper bounds on the execution times of the operators of the types
       Time and Time_Span, in processor clock cycles.

 45.a   Implementation Note:  A fast implementation of the Clock
        function involves repeated reading until you get the same value
        twice.  It is highly improbable that more than three reads will
        be necessary.  Arithmetic on time values should not be
        significantly slower than 64-bit arithmetic in the underlying
        machine instruction set.


                         Implementation Permissions

46   Implementations targeted to machines with word size smaller than 32 bits
need not support the full range and granularity of the Time and Time_Span
types.

        46.a   Discussion:  These requirements are based on machines with a
        word size of 32 bits.

        46.b   Since the range and granularity are implementation defined,
        the supported values need to be documented.
                            Implementation Advice

47   When appropriate, implementations should provide configuration
mechanisms to change the value of Tick.

        47.a   Reason:  This is often needed when the compilation system was
        originally targeted to a particular processor with a particular
        interval timer, but the customer uses the same processor with a
        different interval timer.

        47.b   Discussion:  Tick is a deferred constant and not a named
        number specifically for this purpose.

        47.c   Implementation Note:  This can be achieved either by
        pre-run-time configuration tools, or by having Tick be initialized
        (in the package private part) by a function call residing in a board
        specific module.

48   It is recommended that Calendar.Clock and Real_Time.Clock be implemented
as transformations of the same time base.

49   It is recommended that the ``best'' time base which exists in the
underlying system be available to the application through Clock.  ``Best''
may mean highest accuracy or largest range.


     NOTES
50   (30) The rules in this clause do not imply that the implementation can
     protect the user from operator or installation errors which could result
     in the clock being set incorrectly.

51   (31) Time_Unit is the granularity of the Time type.  In contrast, Tick
     represents the granularity of Real_Time.Clock.  There is no requirement
     that these be the same.



D.9 Delay Accuracy

1   [This clause specifies performance requirements for the delay_statement.
The rules apply both to delay_relative_statement and to delay_until_
statement.  Similarly, they apply equally to a simple delay_statement and to
one which appears in a delay_alternative.]


                              Dynamic Semantics

2   The effect of the delay_statement for Real_Time.Time is defined in terms
of Real_Time.Clock:

    3  If C  is a value of Clock read before a task executes a delay_
           1
       relative_statement with duration D, and C  is a value of Clock
                                                2
       read after the task resumes execution following that delay_
       statement, then C  - C  >= D.
                        2    1
    4  If C is a value of Clock read after a task resumes execution
       following a delay_until_statement with Real_Time.Time value T,
       then C >= T.

5   {potentially blocking operation [delay_statement]} {blocking, potentially
[delay_statement]} A simple delay_statement with a negative or zero value for
the expiration time does not cause the calling task to be blocked; it is
nevertheless a potentially blocking operation (see 9.5.1).

6   When a delay_statement appears in a delay_alternative of a timed_entry_
call the selection of the entry call is attempted, regardless of the
specified expiration time.

        6.a   Ramification:  The effect of these requirements is that one has
        to always attempt a rendezvous, regardless of the value of the delay
        expression.  This can be tested by issuing a timed_entry_call with an
        expiration time of zero, to an open entry.

When a delay_statement appears in a selective_accept_alternative, and a call
is queued on one of the open entries, the selection of that entry call
proceeds, regardless of the value of the delay expression.


                         Documentation Requirements

7   {documentation requirements} The implementation shall document the
minimum value of the delay expression of a delay_relative_statement that
causes the task to actually be blocked.

8   The implementation shall document the minimum difference between the
value of the delay expression of a delay_until_statement and the value of
Real_Time.Clock, that causes the task to actually be blocked.

        8.a   Implementation defined:  Implementation-defined aspects of
        delay_statements.


                                   Metrics

9   {metrics} The implementation shall document the following metrics:

   10  An upper bound on the execution time, in processor clock cycles,
       of a delay_relative_statement whose requested value of the delay
       expression is less than or equal to zero.

   11  An upper bound on the execution time, in processor clock cycles,
       of a delay_until_statement whose requested value of the delay
       expression is less than or equal to the value of Real_Time.Clock
       at the time of executing the statement.  Similarly, for
       Calendar.Clock.

   12  {lateness} {actual duration} An upper bound on the lateness of a
       delay_relative_statement, for a positive value of the delay
       expression, in a situation where the task has sufficient priority
       to preempt the processor as soon as it becomes ready, and does
       not need to wait for any other execution resources.  The upper
       bound is expressed as a function of the value of the delay
       expression.  The lateness is obtained by subtracting the value of
       the delay expression from the actual duration.  The actual
       duration is measured from a point immediately before a task
       executes the delay_statement to a point immediately after the
       task resumes execution following this statement.

   13  An upper bound on the lateness of a delay_until_statement, in a
       situation where the value of the requested expiration time is
       after the time the task begins executing the statement, the task
       has sufficient priority to preempt the processor as soon as it
       becomes ready, and it does not need to wait for any other
       execution resources.  The upper bound is expressed as a function
       of the difference between the requested expiration time and the
       clock value at the time the statement begins execution.  The
       lateness of a delay_until_statement is obtained by subtracting
       the requested expiration time from the real time that the task
       resumes execution following this statement.


     NOTES
14   (32) The execution time of a delay_statement that does not cause the
     task to be blocked (e.g. ``delay 0.0;'' ) is of interest in situations
     where delays are used to achieve voluntary round-robin task dispatching
     among equal-priority tasks.


                         Wording Changes From Ada 83

        14.a   The rules regarding a timed_entry_call with a very small
        positive Duration value, have been tightened to always require the
        check whether the rendezvous is immediately possible.



D.10 Synchronous Task Control

1   [This clause describes a language-defined private semaphore (suspension
object), which can be used for two-stage suspend operations and as a simple
building block for implementing higher-level queues.]


                              Static Semantics

2   The following language-defined package exists:

3   package Ada.Synchronous_Task_Control is

4     type Suspension_Object is limited private;
      procedure Set_True(S : in out Suspension_Object);
      procedure Set_False(S : in out Suspension_Object);
      function Current_State(S : Suspension_Object) return Boolean;
      procedure Suspend_Until_True(S : in out Suspension_Object);
    private
         ... -- not specified by the language
    end Ada.Synchronous_Task_Control;

5   The type Suspension_Object is a by-reference type.

        5.a   Implementation Note:  The implementation can ensure this by,
        for example, making the full view a limited record type.


                              Dynamic Semantics

6   An object of the type Suspension_Object has two visible states: true and
false.  Upon initialization, its value is set to false.

        6.a   Discussion:  This object is assumed to be private to the
        declaring task, i.e. only that task will call Suspend_Until_True on
        this object, and the count of callers is at most one.  Other tasks
        can, of course, change and query the state of this object.

7   The operations Set_True and Set_False are atomic with respect to each
other and with respect to Suspend_Until_True; they set the state to true and
false respectively.

8   Current_State returns the current state of the object.

        8.a   Discussion:  This state can change immediately after the
        operation returns.

9   The procedure Suspend_Until_True blocks the calling task until the state
of the object S is true; at that point the task becomes ready and the state
of the object becomes false.

10   {potentially blocking operation [Suspend_Until_True]} {blocking,
potentially [Suspend_Until_True]} {Program_Error (raised by failure of
run-time check)} Program_Error is raised upon calling Suspend_Until_True if
another task is already waiting on that suspension object.  Suspend_Until_
True is a potentially blocking operation (see 9.5.1).


                         Implementation Requirements

11   The implementation is required to allow the calling of Set_False and
Set_True during any protected action, even one that has its ceiling priority
in the Interrupt_Priority range.



D.11 Asynchronous Task Control

1   [This clause introduces a language-defined package to do asynchronous
suspend/resume on tasks.  It uses a conceptual held priority value to
represent the task's held state.]


                              Static Semantics

2   The following language-defined library package exists:

3   with Ada.Task_Identification;
    package Ada.Asynchronous_Task_Control is
      procedure Hold(T : in Ada.Task_Identification.Task_ID);
      procedure Continue(T : in Ada.Task_Identification.Task_ID);
      function Is_Held(T : Ada.Task_Identification.Task_ID)
       return Boolean;
    end Ada.Asynchronous_Task_Control;


                              Dynamic Semantics

4   {task state [held]} {held priority} {idle task} After the Hold operation
has been applied to a task, the task becomes held.

        4.a   Discussion:  This state should not be confused with the blocked
        state as defined in 9.2; the task is still ready.

For each processor there is a conceptual idle task, which is always ready.
The base priority of the idle task is below System.Any_Priority'First.  The
held priority is a constant of the type integer whose value is below the base
priority of the idle task.

5   The Hold operation sets the state of T to held.  For a held task:  the
task's own base priority does not constitute an inheritance source (see D.1),
and the value of the held priority is defined to be such a source instead.

        5.a   Ramification:  For example, if T is currently inheriting
        priorities from other sources (e.g.  it is executing in a protected
        action), its active priority does not change, and it continues to
        execute until it leaves the protected action.

6   The Continue operation resets the state of T to not-held; T's active
priority is then reevaluated as described in D.1.  [This time, T's base
priority is taken into account.]

7   The Is_Held function returns True if and only if T is in the held state.

        7.a   Discussion:  Note that the state of T can be changed
        immediately after Is_Held returns.

8   As part of these operations, a check is made that the task identified by
T is not terminated.  {Tasking_Error (raised by failure of run-time check)}
Tasking_Error is raised if the check fails.  {Program_Error (raised by
failure of run-time check)} Program_Error is raised if the value of T is
Null_Task_ID.


                             Erroneous Execution

9   {erroneous execution} If any operation in this package is called with a
parameter T that specifies a task object that no longer exists, the execution
of the program is erroneous.


                         Implementation Permissions

10   An implementation need not support Asynchronous_Task_Control if it is
infeasible to support it in the target environment.

        10.a   Reason:  A direct implementation of the Asynchronous_Task_
        Control semantics using priorities is not necessarily efficient
        enough.  Thus, we envision implementations that use some other
        mechanism to set the ``held'' state.  If there is no other such
        mechanism, support for Asynchronous_Task_Control might be infeasible,
        because an implementation in terms of priority would require one idle
        task per processor.  On some systems, programs are not supposed to
        know how many processors are available, so creating enough idle tasks
        would be problematic.


     NOTES
11   (33) It is a consequence of the priority rules that held tasks cannot be
     dispatched on any processor in a partition (unless they are inheriting
     priorities) since their priorities are defined to be below the priority
     of any idle task.

12   (34) The effect of calling Get_Priority and Set_Priority on a Held task
     is the same as on any other task.

13   (35) Calling Hold on a held task or Continue on a non-held task has no
     effect.

14   (36) The rules affecting queuing are derived from the above rules, in
     addition to the normal priority rules:

        15  When a held task is on the ready queue, its priority is so
            low as to never reach the top of the queue as long as there
            are other tasks on that queue.

        16  If a task is executing in a protected action, inside a
            rendezvous, or is inheriting priorities from other sources
            (e.g.  when activated), it continues to execute until it is
            no longer executing the corresponding construct.

        17  If a task becomes held while waiting (as a caller) for a
            rendezvous to complete, the active priority of the accepting
            task is not affected.

        18  If a task becomes held while waiting in a selective_accept,
            and a entry call is issued to one of the open entries, the
            corresponding accept body executes.  When the rendezvous
            completes, the active priority of the accepting task is
            lowered to the held priority (unless it is still inheriting
            from other sources), and the task does not execute until
            another Continue.

        19  The same holds if the held task is the only task on a
            protected entry queue whose barrier becomes open.  The
            corresponding entry body executes.



D.12 Other Optimizations and Determinism Rules

1   [This clause describes various requirements for improving the response
and determinism in a real-time system.]


                         Implementation Requirements

2   If the implementation blocks interrupts (see C.3) not as a result of
direct user action (e.g. an execution of a protected action) there shall be
an upper bound on the duration of this blocking.

        2.a   Ramification:  The implementation shall not allow itself to be
        interrupted when it is in a state where it is unable to support all
        the language-defined operations permitted in the execution of
        interrupt handlers.  (see 9.5.1).

3   The implementation shall recognize entry-less protected types.  The
overhead of acquiring the execution resource of an object of such a type (see
9.5.1) shall be minimized.

        3.a   Implementation Note:  Ideally just a spin-lock.

In particular, there should not be any overhead due to evaluating entry_
barrier conditions.

4   Unchecked_Deallocation shall be supported for terminated tasks that are
designated by access types, and shall have the effect of releasing all the
storage associated with the task.  This includes any run-time system or heap
storage that has been implicitly allocated for the task by the
implementation.


                         Documentation Requirements

5   {documentation requirements} The implementation shall document the upper
bound on the duration of interrupt blocking caused by the implementation.  If
this is different for different interrupts or interrupt priority levels, it
should be documented for each case.

        5.a   Implementation defined:  The upper bound on the duration of
        interrupt blocking caused by the implementation.


                                   Metrics

6   {metrics} The implementation shall document the following metric:

    7  The overhead associated with obtaining a mutual-exclusive access
       to an entry-less protected object.  This shall be measured in the
       following way:

       8   For a protected object of the form:

9          protected Lock is
              procedure Set;
              function Read return Boolean;
           private
              Flag : Boolean := False;
           end Lock;
10         protected body Lock is
              procedure Set is
              begin
                 Flag := True;
              end Set;
              function Read return Boolean
              Begin
                 return Flag;
              end Read;
           end Lock;

       11   The execution time, in processor clock cycles, of a call to
       Set.  This shall be measured between the point just before
       issuing the call, and the point just after the call completes.
       The function Read shall be called later to verify that Set was
       indeed called (and not optimized away).  The calling task shall
       have sufficiently high priority as to not be preempted during the
       measurement period.  The protected object shall have sufficiently
       high ceiling priority to allow the task to call Set.

       12   For a multiprocessor, if supported, the metric shall be
       reported for the case where no contention (on the execution
       resource) exists [from tasks executing on other processors].



                                   Annex E
                                 (normative)


                             Distributed Systems



1   [This Annex defines facilities for supporting the implementation of
distributed systems using multiple partitions working cooperatively as part
of a single Ada program.  {94-4472.a}]


                            Extensions to Ada 83

        1.a   {extensions to Ada 83} This Annex is new to Ada 9X.

                           Post-Compilation Rules

2   {post-compilation rules} {processing node} {storage node} {distributed
system} A distributed system is an interconnection of one or more processing
nodes (a system resource that has both computational and storage
capabilities), and zero or more storage nodes (a system resource that has
only storage capabilities, with the storage addressable by one or more
processing nodes).

3   {distributed program} A distributed program comprises one or more
partitions that execute independently (except when they communicate) in a
distributed system.

4   {configuration (of the partitions of a program)} The process of mapping
the partitions of a program to the nodes in a distributed system is called
configuring the partitions of the program.


                         Implementation Requirements

5   The implementation shall provide means for explicitly assigning library
units to a partition and for the configuring and execution of a program
consisting of multiple partitions on a distributed system; the means are
implementation defined.

        5.a   Implementation defined:  The means for creating and executing
        distributed programs.


                         Implementation Permissions

6   An implementation may require that the set of processing nodes of a
distributed system be homogeneous.


     NOTES
7    (1) The partitions comprising a program may be executed on differently
     configured distributed systems or on a non-distributed system without
     requiring recompilation.  A distributed program may be partitioned
     differently from the same set of library units without recompilation.
     The resulting execution is semantically equivalent.  {94-4890.a}

8    (2) A distributed program retains the same type safety as the equivalent
     single partition program.  {94-4784.a} {94-4788.b} {94-4846.a}



E.1 Partitions

1   [The partitions of a distributed program are classified as either active
or passive.]


                           Post-Compilation Rules

2   {post-compilation rules} {active partition} {passive partition} An active
partition is a partition as defined in 10.2. A passive partition is a
partition that has no thread of control of its own, whose library units are
all preelaborated, and whose data and subprograms are accessible to one or
more active partitions.

        2.a   Discussion:  In most situations, a passive partition does not
        execute, and does not have a ``real'' environment task.  Any
        execution involved in its elaboration and initialization occurs
        before it comes into existence in a distributed program (like most
        preelaborated entities).  Likewise, there is no concrete meaning to
        passive partition termination.

3   A passive partition shall include only library_items that either are
declared pure or are shared passive (see 10.2.1 and E.2.1).

4   An active partition shall be configured on a processing node.  A passive
partition shall be configured either on a storage node or on a processing
node.

5   The configuration of the partitions of a program onto a distributed
system shall be consistent with the possibility for data references or calls
between the partitions implied by their semantic dependences.  {remote
access} Any reference to data or call of a subprogram across partitions is
called a remote access.

        5.a   Discussion:  For example, an active partition that includes a
        unit with a semantic dependence on the declaration of another RCI
        package of some other active partition has to be connected to that
        other partition by some sort of a message passing mechanism.

        5.b   A passive partition that is accessible to an active partition
        should have its storage addressable to the processor(s) of the active
        partition.  The processor(s) should be able to read and write from/to
        that storage, as well as to perform ``read-modify-write'' operations
        (in order to support entry-less protected objects).  {94-4472.f}


                              Dynamic Semantics

6   {elaboration (partition)} A library_item is elaborated as part of the
elaboration of each partition that includes it.  If a normal library unit
(see E.2) has state, then a separate copy of the state exists in each active
partition that elaborates it.  [The state evolves independently in each such
partition.]  {94-4472.g}

        6.a   Ramification:  Normal library units cannot be included in
        passive partitions.

7   {termination (of a partition)} {abort (of a partition)} {inaccessible
partition} {accessible partition} [An active partition terminates when its
environment task terminates.] A partition becomes inaccessible if it
terminates or if it is aborted. An active partition is aborted when its
environment task is aborted. In addition, if a partition fails during its
elaboration, it becomes inaccessible to other partitions. Other
implementation-defined events can also result in a partition becoming
inaccessible.

        7.a   Implementation defined:  Any events that can result in a
        partition becoming inaccessible.

8   For a prefix D that denotes a library-level declaration, excepting a
declaration of or within a declared-pure library unit, the following
attribute is defined:

9   D'Partition_ID
                Denotes a value of the type universal_integer that identifies
                the partition in which D was elaborated.  If D denotes the
                declaration of a remote call interface library unit (see
                E.2.3) the given partition is the one where the body of D was
                elaborated.


                          Bounded (Run-Time) Errors

10   {bounded error} It is a bounded error for there to be cyclic elaboration
dependences between the active partitions of a single distributed program.
{Program_Error (raised by failure of run-time check)} The possible effects
are deadlock during elaboration, or the raising of Program_Error in one or
all of the active partitions involved.


                         Implementation Permissions

11   An implementation may allow multiple active or passive partitions to be
configured on a single processing node, and multiple passive partitions to be
configured on a single storage node.  In these cases, the scheduling
policies, treatment of priorities, and management of shared resources between
these partitions are implementation defined.  {94-4472.i}

        11.a   Implementation defined:  The scheduling policies, treatment of
        priorities, and management of shared resources between partitions in
        certain cases.

12   An implementation may allow separate copies of an active partition to be
configured on different processing nodes, and to provide appropriate
interactions between the copies to present a consistent state of the
partition to other active partitions.

        12.a   Ramification:  The language does not specify the nature of
        these interactions, nor the actual level of consistency preserved.

13   In an implementation, the partitions of a distributed program need not
be loaded and elaborated all at the same time; they may be loaded and
elaborated one at a time over an extended period of time.  An implementation
may provide facilities to abort and reload a partition during the execution
of a distributed program.

14   An implementation may allow the state of some of the partitions of a
distributed program to persist while other partitions of the program
terminate and are later reinvoked.


     NOTES
15   (3) Library units are grouped into partitions after compile time, but
     before run time.  {94-4472.d} At compile time, only the relevant library
     unit properties are identified using categorization pragmas.
     {94-4784.a} {94-4788.b}

16   (4) The value returned by the Partition_ID attribute can be used as a
     parameter to implementation-provided subprograms in order to query
     information about the partition.



E.2 Categorization of Library Units

1   [Library units can be categorized according to the role they play in a
distributed program.  Certain restrictions are associated with each category
to ensure that the semantics of a distributed program remain close to the
semantics for a nondistributed program.]

2   {categorization pragma [distributed]} {pragma, categorization
[distributed]} {library unit pragma [categorization pragmas]} {pragma,
library unit [categorization pragmas]} {categorized library unit} A
categorization pragma is a library unit pragma (see 10.1.5) that restricts
the declarations, child units, or semantic dependences of the library unit to
which it applies. A categorized library unit is a library unit to which a
categorization pragma applies.

3   The pragmas Shared_Passive, Remote_Types, and Remote_Call_Interface are
categorization pragmas.  In addition, for the purposes of this Annex, the
pragma Pure (see 10.2.1) is considered a categorization pragma.

4   {shared passive library unit} A library package or generic library
package is called a shared passive library unit if a Shared_Passive pragma
applies to it.  {remote types library unit} A library package or generic
library package is called a remote types library unit if a Remote_Types
pragma applies to it.  {remote call interface} A library package or generic
library package is called a remote call interface if a Remote_Call_Interface
pragma applies to it.  {normal library unit} A normal library unit is one to
which no categorization pragma applies.  {94-4472.l}

5   [The various categories of library units and the associated restrictions
are described in this clause and its subclauses.  The categories are related
hierarchically in that the library units of one category can depend
semantically only on library units of that category or an earlier one, except
that the body of a remote types or remote call interface library unit is
unrestricted.  {94-4846.b}

6   The overall hierarchy (including declared pure) is as follows:

7   Declared Pure
                Can depend only on other declared pure library units;

8   Shared Passive
                Can depend only on other shared passive or declared pure
                library units;

9   Remote Types
                The declaration of the library unit can depend only on other
                remote types library units, or one of the above; the body of
                the library unit is unrestricted; {94-4657.a} {94-4658.a}
                {94-4672.a} {94-4674.a} {94-4723.a} {94-3786.a} {94-4824.a}

10  Remote Call Interface
                The declaration of the library unit can depend only on other
                remote call interfaces, or one of the above; the body of the
                library unit is unrestricted;

11  Normal
                Unrestricted.

12   Declared pure and shared passive library units are preelaborated.  The
declaration of a remote types or remote call interface library unit is
required to be preelaborable.  {94-4657.a} {94-4658.a} {94-4672.a}
{94-4674.a} {94-4723.a} {94-3786.a} {94-4824.a}]


                         Implementation Requirements

13   For a given library-level type declared in a preelaborated library unit
or in the declaration of a remote types or remote call interface library
unit, the implementation shall choose the same representation for the type
upon each elaboration of the type's declaration for different partitions of
the same program.  {94-4657.a} {94-4658.a} {94-4672.a} {94-4674.a}
{94-4723.a} {94-3786.a} {94-4824.a}


                         Implementation Permissions

14   Implementations are allowed to define other categorization pragmas.



E.2.1 Shared Passive Library Units

1   [A shared passive library unit is used for managing global data shared
between active partitions.  The restrictions on shared passive library units
prevent the data or tasks of one active partition from being accessible to
another active partition through references implicit in objects declared in
the shared passive library unit.]


                         Language Design Principles

        1.a   The restrictions governing a shared passive library unit are
        designed to ensure that objects and subprograms declared in the
        package can be used safely from multiple active partitions, even
        though the active partitions live in different address spaces, and
        have separate run-time systems.

                                   Syntax

    2   {categorization pragma [Shared_Passive]} {pragma, categorization
    [Shared_Passive]} The form of a pragma Shared_Passive is as follows:


3     pragma Shared_Passive[(library_unit_name)];


                               Legality Rules

4   {shared passive library unit} A shared passive library unit is a library
unit to which a Shared_Passive pragma applies.  The following restrictions
apply to such a library unit:

    5  [it shall be preelaborable (see 10.2.1);]

 5.a    Ramification:  It cannot contain library-level declarations of
        protected objects with entries, nor of task objects.  Task
        objects are disallowed because passive partitions don't have any
        threads of control of their own, nor any run-time system of
        their own.  {94-4472.n} Protected objects with entries are
        disallowed because an entry queue contains references to calling
        tasks, and that would require in effect a pointer from a passive
        partition back to a task in some active partition.

    6  it shall depend semantically only upon declared pure or shared
       passive library units;

 6.a    Reason:  Shared passive packages cannot depend semantically upon
        remote types packages because the values of an access type
        declared in a remote types package refer to the local heap of
        the active partition including the remote types package.

    7  it shall not contain a library-level declaration of an access
       type that designates a class-wide type, task type, or protected
       type with entry_declarations; if the shared passive library unit
       is generic, it shall not contain a declaration for such an access
       type unless the declaration is nested within a body other than a
       package_body.

 7.a    Reason:  These kinds of access types are disallowed because the
        object designated by an access value of such a type could
        contain an implicit reference back to the active partition on
        whose behalf the designated object was created.

8   {accessibility [from shared passive library units]} {notwithstanding}
Notwithstanding the definition of accessibility given in 3.10.2, the
declaration of a library unit P1 is not accessible from within the
declarative region of a shared passive library unit P2, unless the shared
passive library unit P2 depends semantically on P1.

        8.a   Discussion:  We considered a more complex rule, but dropped it.
        This is the simplest rule that recognizes that a shared passive
        package may outlive some other library package, unless it depends
        semantically on that package.  In a nondistributed program, all
        library packages are presumed to have the same lifetime.

        8.b   Implementations may define additional pragmas that force two
        library packages to be in the same partition, or to have the same
        lifetime, which would allow this rule to be relaxed in the presence
        of such pragmas.


                              Static Semantics

9   {preelaborated [partial]} A shared passive library unit is preelaborated.


                           Post-Compilation Rules

10   {post-compilation rules} A shared passive library unit shall be assigned
to at most one partition within a given program.

11   {compilation units needed [shared passive library unit]} {needed [shared
passive library unit]} {notwithstanding} Notwithstanding the rule given in
10.2, a compilation unit in a given partition does not need (in the sense of
10.2) the shared passive library units on which it depends semantically to be
included in that same partition; they will typically reside in separate
passive partitions.  {94-4768.v} {94-4673.a} {94-4769.a}



E.2.2 Remote Types Library Units

1   [A remote types library unit supports the definition of types intended
for use in communication between active partitions.]


                         Language Design Principles

        1.a   The restrictions governing a remote types package are similar
        to those for a declared pure package. However, the restrictions are
        relaxed deliberately to allow such a package to contain declarations
        that violate the stateless property of pure packages, though it is
        presumed that any state-dependent properties are essentially
        invisible outside the package.

                                   Syntax

    2   {categorization pragma [Remote_Types]} {pragma, categorization
    [Remote_Types]} The form of a pragma Remote_Types is as follows:


3     pragma Remote_Types[(library_unit_name)];


                               Legality Rules

4   {remote types library unit} A remote types library unit is a library unit
to which the pragma Remote_Types applies.  The following restrictions apply
to the declaration of such a library unit:  {94-4657.a} {94-4658.a}
{94-4672.a} {94-4674.a} {94-4723.a} {94-3786.a} {94-4824.a}

    5  [it shall be preelaborable;]

    6  it shall depend semantically only on declared pure, shared
       passive, or other remote types library units;

    7  it shall not contain the declaration of any variable within the
       visible part of the library unit; {94-4657.a} {94-4658.a}
       {94-4672.a} {94-4674.a} {94-4723.a} {94-3786.a} {94-4824.a}

 7.a    Reason:  This is essentially a ``methodological'' restriction.
        A separate copy of a remote types package is included in each
        partition that references it, just like a normal package.
        Nevertheless, a remote types package is thought of as an
        ``essentially pure'' package for defining types to be used for
        interpartition communication, and it could be misleading to
        declare visible objects when no remote data access is actually
        being provided.

    8  if the full view of a type declared in the visible part of the
       library unit has a part that is of a non-remote access type, then
       that access type, or the type of some part that includes the
       access type subcomponent, shall have user-specified Read and
       Write attributes.

 8.a    Reason:  This is to prevent the use of the predefined Read and
        Write attributes of an access type as part of the Read and Write
        attributes of a visible type.


{remote access type} An access type declared in the visible part of a remote
types or remote call interface library unit is called a remote access type.
{remote access-to-subprogram type} {remote access-to-class-wide type} Such a
type shall be either an access-to-subprogram type or a general access type
that designates a class-wide limited private type.  {94-4657.a} {94-4658.a}
{94-4672.a} {94-4674.a} {94-4723.a} {94-3786.a} {94-4824.a}

The following restrictions apply to the use of a remote access-to-subprogram
type:

    9  A value of a remote access-to-subprogram type shall be converted
       only to another (subtype-conformant) remote access-to-subprogram
       type;

   10  The prefix of an Access attribute_reference that yields a value
       of a remote access-to-subprogram type shall statically denote a
       (subtype-conformant) remote subprogram.

The following restrictions apply to the use of a remote access-to-class-wide
type:

   11  The primitive subprograms of the corresponding specific limited
       private type shall only have access parameters if they are
       controlling formal parameters; the types of all the
       non-controlling formal parameters shall have Read and Write
       attributes.

   12  A value of a remote access-to-class-wide type shall be explicitly
       converted only to another remote access-to-class-wide type;

   13  A value of a remote access-to-class-wide type shall be
       dereferenced (or implicitly converted to an anonymous access
       type) only as part of a dispatching call where the value
       designates a controlling operand of the call (see E.4, ``Remote
       Subprogram Calls'');

   14  The Storage_Pool and Storage_Size attributes are not defined for
       remote access-to-class-wide types; the expected type for an
       allocator shall not be a remote access-to-class-wide type; a
       remote access-to-class-wide type shall not be an actual parameter
       for a generic formal access type;

 14.a   Reason:  All three of these restrictions are because there is no
        storage pool associated with a remote access-to-class-wide type.


     NOTES
15   (5) A remote types library unit need not be pure, and the types it
     defines may include levels of indirection implemented by using access
     types.  User-specified Read and Write attributes (see 13.13.2) provide
     for sending values of such a type between active partitions, with Write
     marshalling the representation, and Read unmarshalling any levels of
     indirection.



E.2.3 Remote Call Interface Library Units

1   [A remote call interface library unit can be used as an interface for
remote procedure calls (RPCs) (or remote function calls) between active
partitions.]


                         Language Design Principles

        1.a   The restrictions governing a remote call interface library unit
        are intended to ensure that the values of the actual parameters in a
        remote call can be meaningfully sent between two active partitions.

                                   Syntax

    2   {categorization pragma [Remote_Call_Interface]} {pragma,
    categorization [Remote_Call_Interface]} The form of a pragma Remote_Call_
    Interface is as follows:


3     pragma Remote_Call_Interface[(library_unit_name)];

    4   The form of a pragma All_Calls_Remote is as follows:


5     pragma All_Calls_Remote[(library_unit_name)];

    6   {library unit pragma [All_Calls_Remote]} {pragma, library unit [All_
    Calls_Remote]} A pragma All_Calls_Remote is a library unit pragma.
    {94-4786.a} {94-4787.a} {94-4788.c}


                               Legality Rules

7   {remote call interface} {RCI (library unit)} {RCI (package)} {RCI
(generic)} {remote subprogram} A remote call interface (RCI) is a library
unit to which the pragma Remote_Call_Interface applies.  A subprogram
declared in the visible part of such a library unit is called a remote
subprogram.  {94-4657.a} {94-4658.a} {94-4672.a} {94-4674.a} {94-4723.a}
{94-3786.a} {94-4824.a}

8   The declaration of an RCI library unit shall be preelaborable (see
10.2.1), and shall depend semantically only upon declared pure, shared
passive, remote types, or other remote call interface library units.

9   In addition, the following restrictions apply to the visible part of an
RCI library unit:

   10  it shall not contain the declaration of a variable;

 10.a   Reason:  Remote call interface packages do not provide remote
        data access.  A shared passive package has to be used for that.

   11  it shall not contain the declaration of a limited type;

 11.a   Reason:  We disallow the declaration of task and protected
        types, since calling an entry or a protected subprogram
        implicitly passes an object of a limited type (the target task
        or protected object).  We disallow other limited types since we
        require that such types have user-defined Read and Write
        attributes, but we certainly don't want the Read and Write
        attributes themselves to involve remote calls (thereby defeating
        their purpose of marshalling the value for remote calls).

   12  it shall not contain a nested generic_declaration;

 12.a   Reason:  This is disallowed because the body of the nested
        generic would presumably have access to data inside the body of
        the RCI package, and if instantiated in a different partition,
        remote data access might result, which is not supported.

   13  it shall not contain the declaration of a subprogram to which a
       pragma Inline applies;

   14  it shall not contain a subprogram (or access-to-subprogram)
       declaration whose profile has an access parameter, or a formal
       parameter of a limited type unless that limited type has
       user-specified Read and Write attributes; {94-4657.a} {94-4658.a}
       {94-4672.a} {94-4674.a} {94-4723.a} {94-3786.a} {94-4824.a}

   15  any public child of the library unit shall be a remote call
       interface library unit.

 15.a   Reason:  No restrictions apply to the private part of an RCI
        package, and since a public child can ``see'' the private part
        of its parent, such a child must itself have a Remote_Call_
        Interface pragma, and be assigned to the same partition (see
        below).  {94-4472.q}

 15.b   Discussion:  We considered making the public child of an RCI
        package implicitly RCI, but it seemed better to require an
        explicit pragma to avoid any confusion.

 15.c   Note that there is no need for a private child to be an RCI
        package, since it can only be seen from the body of its parent
        or its siblings, all of which are required to be in the same
        active partition.

16   If a pragma All_Calls_Remote applies to a library unit, the library unit
shall be a remote call interface.


                           Post-Compilation Rules

17   {post-compilation rules} A remote call interface library unit shall be
assigned to at most one partition of a given program.  A remote call
interface library unit whose parent is also an RCI library unit shall be
assigned only to the same partition as its parent.

        17.a   Implementation Note:  The declaration of an RCI package, with
        a calling-stub body, is automatically included in all active
        partitions with compilation units that depend on it.  However the
        whole RCI library unit, including its (non-stub) body, will only be
        in one of the active partitions.

18   {compilation units needed [remote call interface]} {needed [remote call
interface]} {notwithstanding} Notwithstanding the rule given in 10.2, a
compilation unit in a given partition that semantically depends on the
declaration of an RCI library unit, needs (in the sense of 10.2) only the
declaration of the RCI library unit, not the body, to be included in that
same partition.  [Therefore, the body of an RCI library unit is included only
in the partition to which the RCI library unit is explicitly assigned.]


                         Implementation Requirements

19   If a pragma All_Calls_Remote applies to a given RCI library package,
then the implementation shall route any call to a subprogram of the RCI
package from outside the declarative region of the package through the
Partition Communication Subsystem (PCS); see E.5.  Calls to such subprograms
from within the declarative region of the package are defined to be local and
shall not go through the PCS.  {94-4472.r} {94-4887.a}

        19.a   Discussion:  Without this pragma, it is presumed that most
        implementations will make direct calls if the call originates in the
        same partition as that of the RCI package.  With this pragma, all
        calls from outside the subsystem rooted at the RCI package are
        treated like calls from outside the partition, ensuring that the PCS
        is involved in all such calls (for debugging, redundancy, etc.).

        19.b   Reason:  There is no point to force local calls (or calls from
        children) to go through the PCS, since on the target system, these
        calls are always local, and all the units are in the same active
        partition.


                         Implementation Permissions

20   An implementation need not support the Remote_Call_Interface pragma nor
the All_Calls_Remote pragma.  [Explicit message-based communication between
active partitions can be supported as an alternative to RPC.]

        20.a   Ramification:  Of course, it is pointless to support the All_
        Calls_Remote pragma if the Remote_Call_Interface pragma (or some
        approximate equivalent) is not supported.



E.3 Consistency of a Distributed System

1   [This clause defines attributes and rules associated with verifying the
consistency of a distributed program.  {94-4472.s}]


                         Language Design Principles

        1.a   The rules guarantee that remote call interface and shared
        passive packages are consistent among all partitions prior to the
        execution of a distributed program, so that the semantics of the
        distributed program are well defined.

                              Static Semantics

2   For a prefix P that statically denotes a program unit, the following
attributes are defined:

3   P'Version
                Yields a value of the predefined type String that identifies
                the version of the compilation unit that contains the
                declaration of the program unit.

4   P'Body_Version
                Yields a value of the predefined type String that identifies
                the version of the compilation unit that contains the body
                (but not any subunits) of the program unit.

5   {version (of a compilation unit)} The version of a compilation unit
changes whenever the version changes for any compilation unit on which it
depends semantically.  The version also changes whenever the compilation unit
itself changes in a semantically significant way.  It is implementation
defined whether there are other events (such as recompilation) that result in
the version of a compilation unit changing.

        5.a   Implementation defined:  Events that cause the version of a
        compilation unit to change.


                          Bounded (Run-Time) Errors

6   {bounded error} {unit consistency} In a distributed program, a library
unit is consistent if the same version of its declaration is used throughout.
It is a bounded error to elaborate a partition of a distributed program that
contains a compilation unit that depends on a different version of the
declaration of a shared passive or RCI library unit than that included in the
partition to which the shared passive or RCI library unit was assigned.
{Program_Error (raised by failure of run-time check)} As a result of this
error, Program_Error can be raised in one or both partitions during
elaboration; in any case, the partitions become inaccessible to one another.

        6.a   Ramification:  Because a version changes if anything on which
        it depends undergoes a version change, requiring consistency for
        shared passive and remote call interface library units is sufficient
        to ensure consistency for the declared pure and remote types library
        units that define the types used for the objects and parameters
        through which interpartition communication takes place.

        6.b   Note that we do not require matching Body_Versions; it is
        irrelevant for shared passive and remote call interface packages,
        since only one copy of their body exists in a distributed program (in
        the absence of implicit replication), and we allow the bodies to
        differ for declared pure and remote types packages from partition to
        partition, presuming that the differences are due to required error
        corrections that took place during the execution of a long-running
        distributed program.  The Body_Version attribute provides a means for
        performing stricter consistency checks.



E.4 Remote Subprogram Calls

1   {remote subprogram call} {asynchronous remote procedure call
[distributed]} {calling partition} {called partition} {remote subprogram
binding} A remote subprogram call is a subprogram call that invokes the
execution of a subprogram in another partition.  The partition that
originates the remote subprogram call is the calling partition, and the
partition that executes the corresponding subprogram body is the called
partition.  Some remote procedure calls are allowed to return prior to the
completion of subprogram execution. These are called asynchronous remote
procedure calls.

2   There are three different ways of performing a remote subprogram call:

    3  As a direct call on a (remote) subprogram explicitly declared in
       a remote call interface;

    4  As an indirect call through a value of a remote
       access-to-subprogram type;

    5  As a dispatching call with a controlling operand designated by a
       value of a remote access-to-class-wide type.

6   The first way of calling corresponds to a static binding between the
calling and the called partition.  The latter two ways correspond to a
dynamic binding between the calling and the called partition.

7   A remote call interface library unit (see E.2.3) defines the remote
subprograms or remote access types used for remote subprogram calls.


                         Language Design Principles

        7.a   Remote subprogram calls are standardized since the RPC paradigm
        is widely-used, and establishing an interface to it in the annex will
        increase the portability and reusability of distributed programs.
        {94-4472.v}

                               Legality Rules

8   In a dispatching call with two or more controlling operands, if one
controlling operand is designated by a value of a remote access-to-class-wide
type, then all shall be.


                              Dynamic Semantics

9   {marshalling} {unmarshalling} {execution [remote subprogram call]} For
the execution of a remote subprogram call, subprogram parameters (and later
the results, if any) are passed using a stream-oriented representation (see
13.13.1) [which is suitable for transmission between partitions].  This
action is called marshalling. Unmarshalling is the reverse action of
reconstructing the parameters or results from the stream-oriented
representation.[Marshalling is performed initially as part of the remote
subprogram call in the calling partition; unmarshalling is done in the called
partition.  After the remote subprogram completes, marshalling is performed
in the called partition, and finally unmarshalling is done in the calling
partition.]

10   {calling stub} {receiving stub} A calling stub is the sequence of code
that replaces the subprogram body of a remotely called subprogram in the
calling partition. A receiving stub is the sequence of code (the ``wrapper'')
that receives a remote subprogram call on the called partition and invokes
the appropriate subprogram body.

        10.a   Discussion:  The use of the term stub in this annex should not
        be confused with body_stub as defined in 10.1.3.  The term stub is
        used here because it is a commonly understood term when talking about
        the RPC paradigm.

11   {at-most-once execution} Remote subprogram calls are executed at most
once, that is, if the subprogram call returns normally, then the called
subprogram's body was executed exactly once.

12   The task executing a remote subprogram call blocks until the subprogram
in the called partition returns, unless the call is asynchronous. For an
asynchronous remote procedure call, the calling task can become ready before
the procedure in the called partition returns.

13   {cancellation of a remote subprogram call} If a construct containing a
remote call is aborted, the remote subprogram call is cancelled.  Whether the
execution of the remote subprogram is immediately aborted as a result of the
cancellation is implementation defined.

        13.a   Implementation defined:  Whether the execution of the remote
        subprogram is immediately aborted as a result of cancellation.

14   If a remote subprogram call is received by a called partition before the
partition has completed its elaboration, the call is kept pending until the
called partition completes its elaboration (unless the call is cancelled by
the calling partition prior to that).

15   If an exception is propagated by a remotely called subprogram, and the
call is not an asynchronous call, the corresponding exception is reraised at
the point of the remote subprogram call.  For an asynchronous call, if the
remote procedure call returns prior to the completion of the remotely called
subprogram, any exception is lost.

16   The exception Communication_Error (see E.5) is raised if a remote call
cannot be completed due to difficulties in communicating with the called
partition.

17   {potentially blocking operation [remote subprogram call]} {blocking,
potentially [remote subprogram call]} All forms of remote subprogram calls
are potentially blocking operations (see 9.5.1).

        17.a   Reason:  Asynchronous remote procedure calls are potentially
        blocking since the implementation may require waiting for the
        availability of shared resources to initiate the remote call.

18   {Accessibility_Check [partial]} {check, language-defined (Accessibility_
Check)} In a remote subprogram call with a formal parameter of a class-wide
type, a check is made that the tag of the actual parameter identifies a
tagged type declared in a declared-pure or shared passive library unit, or in
the visible part of a remote types or remote call interface library unit.
{94-4472.z} {Program_Error (raised by failure of run-time check)} Program_
Error is raised if this check fails.

        18.a   Discussion:  This check makes certain that the specific type
        passed in an RPC satisfies the rules for a "communicable" type.
        Normally this is guaranteed by the compile-time restrictions on
        remote call interfaces.  However, with class-wide types, it is
        possible to pass an object whose tag identifies a type declared
        outside the "safe" packages.

        18.b   This is considered an accessibility_check since only the types
        declared in "safe" packages are considered truly "global"
        (cross-partition).  Other types are local to a single partition.
        This is analogous to the "accessibility" of global vs. local
        declarations in a single-partition program.

        18.c   This rule replaces a rule from an earlier version of Ada 9X
        which was given in the subclause on Remote Types Library Units (now
        E.2.2, ``Remote Types Library Units'').  That rule tried to prevent
        "bad" types from being sent by arranging for their tags to mismatch
        between partitions.  However, that interfered with other uses of
        tags.  The new rule allows tags to agree in all partitions, even for
        those types which are not "safe" to pass in an RPC.  {94-4472.za}

19   {Partition_Check [partial]} {check, language-defined (Partition_Check)}
In a dispatching call with two or more controlling operands that are
designated by values of a remote access-to-class-wide type, a check is made
[(in addition to the normal Tag_Check -- see 11.5)] that all the remote
access-to-class-wide values originated from Access attribute_references that
were evaluated by tasks of the same active partition.  {Constraint_Error
(raised by failure of run-time check)} Constraint_Error is raised if this
check fails.

        19.a   Implementation Note:  When a remote access-to-class-wide value
        is created by an Access attribute_reference, the identity of the
        active partition that evaluated the attribute_reference should be
        recorded in the representation of the remote access value.


                         Implementation Requirements

20   The implementation of remote subprogram calls shall conform to the PCS
interface as defined by the specification of the language-defined package
System.RPC (see E.5).  The calling stub shall use the Do_RPC procedure unless
the remote procedure call is asynchronous in which case Do_APC shall be used.
On the receiving side, the corresponding receiving stub shall be invoked by
the RPC-receiver.

        20.a   Implementation Note:  One possible implementation model is as
        follows:

        20.b   The code for calls to subprograms declared in an RCI package
        is generated normally, that is, the call-site is the same as for a
        local subprogram call.  The code for the remotely callable subprogram
        bodies is also generated normally.  Subprogram's prologue and
        epilogue are the same as for a local call.

        20.c   When compiling the specification of an RCI package, the
        compiler generates calling stubs for each visible subprogram.
        Similarly, when compiling the body of an RCI package, the compiler
        generates receiving stubs for each visible subprogram together with
        the appropriate tables to allow the RPC-receiver to locate the
        correct receiving stub.

        20.d   For the statically bound remote calls, the identity of the
        remote partition is statically determined (it is resolved at
        configuration/link time).

        20.e   The calling stub operates as follows:

         20.f  It allocates (or reuses) a stream of Params_Stream_Type
               of Initial_Size, and initializes it by repeatedly calling
               Write operations, first to identify which remote
               subprogram in the receiving partition is being called,
               and then to pass the incoming value of each of the in and
               in out parameters of the call.

         20.g  It allocates (or reuses) a stream for the Result, unless
               a pragma Asynchronous is applied to the procedure.
               {94-4472.zb}

         20.h  It calls Do_RPC unless a pragma Asynchronous is applied
               to the procedure in which case it calls Do_APC. An access
               value designating the message stream allocated and
               initialized above is passed as the Params parameter.  An
               access value designating the Result stream is passed as
               the Result parameter.  {94-4472.zb}

         20.i  If the pragma Asynchronous is not specified for the
               procedure, Do_RPC blocks until a reply message arrives,
               and then returns to the calling stub.  {94-4472.zc} The
               stub returns after extracting from the Result stream,
               using Read operations, the in out and out parameters or
               the function result.  If the reply message indicates that
               the execution of the remote subprogram propagated an
               exception, the exception is propagated from Do_RPC to the
               calling stub, and thence to the point of the original
               remote subprogram call.  If Do_RPC detects that
               communication with the remote partition has failed, it
               propagates Communication_Error.

        20.j   On the receiving side, the RPC-receiver procedure operates as
        follows:

         20.k  It is called from the PCS when a remote-subprogram-call
               message is received.  The call originates in some remote
               call receiver task executed and managed in the context of
               the PCS.

         20.l  It extracts information from the stream to identify the
               appropriate receiving stub.

         20.m  The receiving stub extracts the in and in out parameters
               using Read from the stream designated by the Params
               parameter.

         20.n  The receiving stub calls the actual subprogram body and,
               upon completion of the subprogram, uses Write to insert
               the results into the stream pointed to by the Result
               parameter.  The receiving stub returns to the
               RPC-receiver procedure which in turn returns to the PCS.
               If the actual subprogram body propagates an exception, it
               is propagated by the RPC-receiver to the PCS, which
               handles the exception, and indicates in the reply message
               that the execution of the subprogram body propagated an
               exception.  The exception occurrence can be represented
               in the reply message using the Write attribute of
               Ada.Exceptions.Exception_Occurrence.

        20.o   For remote access-to-subprogram types:

        20.p   A value of a remote access-to-subprogram type can be
        represented by the following components: a reference to the remote
        partition, an index to the package containing the remote subprogram,
        and an index to the subprogram within the package.  The values of
        these components are determined at run time when the remote access
        value is created.  These three components serve the same purpose when
        calling Do_APC/RPC, as in the statically bound remote calls; the only
        difference is that they are evaluated dynamically.

        20.q   For remote access-to-class-wide types:

        20.r   For each remote access-to-class-wide type, a calling stub is
        generated for each dispatching operation of the designated type. In
        addition, receiving stubs are generated to perform the remote
        dispatching operations in the called partition.  The appropriate
        subprogram_body is determined as for a local dispatching call once
        the receiving stub has been reached.  {94-4472.zf}

        20.s   A value of a remote access-to-class-wide type can be
        represented with the following components:  a reference to the remote
        partition, an index to a table (created one per each such access
        type) containing addresses of all the dispatching operations of the
        designated type, and an access value designating the actual remote
        object.

        20.t   Alternatively, a remote access-to-class-wide value can be
        represented as a normal access value, pointing to a "stub" object
        which in turn contains the information mentioned above.  A call on
        any dispatching operation of such a stub object does the remote call,
        if necessary, using the information in the stub object to locate the
        target partition, etc.  This approach has the advantage that less
        special-casing is required in the compiler.  All access values can
        remain just a simple address.

        20.u   {Constraint_Error (raised by failure of run-time check)} For a
        call to Do_RPC or Do_APC: The partition ID of all controlling
        operands are checked for equality (a Constraint_Error is raised if
        this check fails). The partition ID value is used for the Partition
        parameter.  An index into the tagged-type-descriptor is created.
        This index points to the receiving stub of the class-wide operation.
        This index and the index to the table (described above) are written
        to the stream.  Then, the actual parameters are marshalled into the
        message stream.  For a controlling operand, only the access value
        designating the remote object is required (the other two components
        are already present in the other parameters).

        20.v   On the called partition (after the RPC-receiver has
        transferred control to the appropriate receiving stub) the parameters
        are first unmarshalled.  Then, the tags of the controlling operands
        (obtained by dereferencing the pointer to the object) are checked for
        equality.  {Constraint_Error (raised by failure of run-time check)}
        If the check fails Constraint_Error is raised and propagated back to
        the calling partition, unless it is a result of an asynchronous call.
        Finally, a dispatching call to the specific subprogram (based on the
        controlling object's tag) is made. Note that since this subprogram is
        not in an RCI package, no specific stub is generated for it, it is
        called normally from the dispatching stub.


     NOTES
21   (6) A given active partition can both make and receive remote subprogram
     calls.  Thus, an active partition can act as both a client and a server.

22   (7) If a given exception is propagated by a remote subprogram call, but
     the exception does not exist in the calling partition, the exception can
     be handled by an others choice or be propagated to and handled by a
     third partition.

   22.a   Discussion:  This situation can happen in a case of dynamically
        nested remote subprogram calls, where an intermediate call executes
        in a partition that does not include the library unit that defines
        the exception.



E.4.1 Pragma Asynchronous

1   [This subclause introduces the pragma Asynchronous which allows a remote
subprogram call to return prior to completion of the execution of the
corresponding remote subprogram body.]


                                   Syntax

    2   The form of a pragma Asynchronous is as follows:


3     pragma Asynchronous(local_name);


                               Legality Rules

4   The local_name of a pragma Asynchronous shall denote either:

    5  One or more remote procedures; the formal parameters of the
       procedure(s) shall all be of mode in;

    6  The first subtype of a remote access-to-procedure type; the
       formal parameters of the designated profile of the type shall all
       be of mode in;

    7  The first subtype of a remote access-to-class-wide type.


                              Static Semantics

8   {representation pragma [Asynchronous]} {pragma, representation
[Asynchronous]} A pragma Asynchronous is a representation pragma.  When
applied to a type, it specifies the type-related asynchronous aspect of the
type.


                              Dynamic Semantics

9   {remote procedure call (asynchronous)} {asynchronous (remote procedure
call)} A remote call is asynchronous if it is a call to a procedure, or a
call through a value of an access-to-procedure type, to which a pragma
Asynchronous applies.  In addition, if a pragma Asynchronous applies to a
remote access-to-class-wide type, then a dispatching call on a procedure with
a controlling operand designated by a value of the type is asynchronous if
the formal parameters of the procedure are all of mode in.  {94-4768.h}


                         Implementation Requirements

10   Asynchronous remote procedure calls shall be implemented such that the
corresponding body executes at most once as a result of the call.

        10.a   To be honest:  It is not clear that this rule can be tested or
        even defined formally.



E.4.2 Example of Use of a Remote Access-to-Class-Wide Type

                                  Examples

1   Example of using a remote access-to-class-wide type to achieve dynamic
binding across active partitions:

2   package Tapes is
       pragma Pure(Tapes);
       type Tape is abstract tagged limited private;
       -- Primitive dispatching operations where
       -- Tape is controlling operand
       procedure Copy (From, To : access Tape; Num_Recs : in Natural) is abstra\
ct;
       procedure Rewind (T : access Tape) is abstract;
       -- More operations
    private
       type Tape is ...
    end Tapes;

3   with Tapes;
    package Name_Server is
       pragma Remote_Call_Interface;
       -- Dynamic binding to remote operations is achieved
       -- using the access-to-limited-class-wide type Tape_Ptr
       type Tape_Ptr is access all Tapes.Tape'Class;
       -- The following statically bound remote operations
       -- allow for a name-server capability in this example
       function  Find     (Name : String) return Tape_Ptr;
       procedure Register (Name : in String; T : in Tape_Ptr);
       procedure Remove   (T : in Tape_Ptr);
       -- More operations
    end Name_Server;

4   package Tape_Driver is
      -- Declarations are not shown, they are irrelevant here
    end Tape_Driver;

5   with Tapes, Name_Server;
    package body Tape_Driver is
       type New_Tape is new Tapes.Tape with ...
       procedure Copy
        (From, To : access New_Tape; Num_Recs: in Natural) is
       begin
         . . .
       end Copy;
       procedure Rewind (T : access New_Tape) is
       begin
          . . .
       end Rewind;
       -- Objects remotely accessible through use
       -- of Name_Server operations
       Tape1, Tape2 : aliased New_Tape;
    begin
       Name_Server.Register ("NINE-TRACK",  Tape1'Access);
       Name_Server.Register ("SEVEN-TRACK", Tape2'Access);
    end Tape_Driver;

6   with Tapes, Name_Server;
    -- Tape_Driver is not needed and thus not mentioned in the with_clause
    procedure Tape_Client is
       T1, T2 : Name_Server.Tape_Ptr;
    begin
       T1 := Name_Server.Find ("NINE-TRACK");
       T2 := Name_Server.Find ("SEVEN-TRACK");
       Tapes.Rewind (T1);
       Tapes.Rewind (T2);
       Tapes.Copy (T1, T2, 3);
    end Tape_Client;

7   Notes on the example:
        7.a   Discussion:  The example does not show the case where tapes are
        removed from or added to the system.  In the former case, an
        appropriate exception needs to be defined to instruct the client to
        use another tape.  In the latter, the Name_Server should have a query
        function visible to the clients to inform them about the availability
        of the tapes in the system.

8

    9  The package Tapes provides the necessary declarations of the type
       and its primitive operations.

   10  Name_Server is a remote call interface package and is elaborated
       in a separate active partition to provide the necessary naming
       services (such as Register and Find) to the entire distributed
       program through remote subprogram calls.

   11  Tape_Driver is a normal package that is elaborated in a partition
       configured on the processing node that is connected to the tape
       device(s). The abstract operations are overridden to support the
       locally declared tape devices (Tape1, Tape2). The package is not
       visible to its clients, but it exports the tape devices (as
       remote objects) through the services of the Name_Server. This
       allows for tape devices to be dynamically added, removed or
       replaced without requiring the modification of the clients' code.

   12  The Tape_Client procedure references only declarations in the
       Tapes and Name_Server packages.  Before using a tape for the
       first time, it needs to query the Name_Server for a system-wide
       identity for that tape. From then on, it can use that identity to
       access the tape device.

   13  Values of remote access type Tape_Ptr include the necessary
       information to complete the remote dispatching operations that
       result from dereferencing the controlling operands T1 and T2.



E.5 Partition Communication Subsystem

1   {partition communication subsystem (PCS)} {PCS (partition communication
subsystem)}[The Partition Communication Subsystem (PCS) provides facilities
for supporting communication between the active partitions of a distributed
program.  The package System.RPC is a language-defined interface to the PCS.]

        1.a   Reason:  The prefix RPC is used rather than RSC because the
        term remote procedure call and its acronym are more familiar.

An implementation conforming to this Annex shall use the RPC interface to
implement remote subprogram calls.


                              Static Semantics

2   The following language-defined library package exists:

3   with Ada.Streams; -- see 13.13.1
    package System.RPC is

4      type Partition_ID is range 0 .. implementation-defined;

5      Communication_Error : exception;

6      type Params_Stream_Type(
          Initial_Size : Ada.Streams.Stream_Element_Count) is new
          Ada.Streams.Root_Stream_Type with private;

7      procedure Read(
          Stream : in out Params_Stream_Type;
          Item : out Ada.Streams.Stream_Element_Array;
          Last : out Ada.Streams.Stream_Element_Offset);

8      procedure Write(
          Stream : in out Params_Stream_Type;
          Item : in Ada.Streams.Stream_Element_Array);

9      -- Synchronous call
       procedure Do_RPC(
          Partition  : in Partition_ID;
          Params     : access Params_Stream_Type;
          Result     : access Params_Stream_Type);

10     -- Asynchronous call
       procedure Do_APC(
          Partition  : in Partition_ID;
          Params     : access Params_Stream_Type);

11     -- The handler for incoming RPCs
       type RPC_Receiver is access procedure(
          Params     : access Params_Stream_Type;
          Result     : access Params_Stream_Type);

12     procedure Establish_RPC_Receiver(
          Partition : in Partition_ID;{94-4553.a}
          Receiver  : in RPC_Receiver);

13  private
       ... -- not specified by the language
    end System.RPC;

14   A value of the type Partition_ID is used to identify a partition.

15   An object of the type Params_Stream_Type is used for identifying the
particular remote subprogram that is being called, as well as marshalling and
unmarshalling the parameters or result of a remote subprogram call, as part
of sending them between partitions.

16   [The Read and Write procedures override the corresponding abstract
operations for the type Params_Stream_Type.]


                              Dynamic Semantics

17   The Do_RPC and Do_APC procedures send a message to the active partition
identified by the Partition parameter.

        17.a   Implementation Note:  It is assumed that the RPC interface is
        above the message-passing layer of the network protocol stack and is
        implemented in terms of it.

18   After sending the message, Do_RPC blocks the calling task until a reply
message comes back from the called partition or some error is detected by the
underlying communication system in which case Communication_Error is raised
at the point of the call to Do_RPC.

        18.a   Reason:  Only one exception is defined in System.RPC, although
        many sources of errors might exist.  This is so because it is not
        always possible to distinguish among these errors.  In particular, it
        is often impossible to tell the difference between a failing
        communication link and a failing processing node.  Additional
        information might be associated with a particular Exception_
        Occurrence for a Communication_Error.

19   Do_APC operates in the same way as Do_RPC except that it is allowed to
return immediately after sending the message.

20   Upon normal return, the stream designated by the Result parameter of Do_
RPC contains the reply message.

21   {elaboration [partition]} The procedure System.RPC.Establish_RPC_
Receiver is called once, immediately after elaborating the library units of
an active partition (that is, right after the elaboration of the partition)
if the partition includes an RCI library unit, but prior to invoking the main
subprogram, if any.  The Partition parameter is the Partition_ID of the
active partition being elaborated.  {94-4553.a} {94-4523.a} {94-4540.a}
{94-4541.a} {94-4542.a} {RPC-receiver} The Receiver parameter designates an
implementation-provided procedure called the RPC-receiver which will handle
all RPCs received by the partition from the PCS.  Establish_RPC_Receiver
saves a reference to the RPC-receiver; when a message is received at the
called partition, the RPC-receiver is called with the Params stream
containing the message. When the RPC-receiver returns, the contents of the
stream designated by Result is placed in a message and sent back to the
calling partition.

        21.a   Implementation Note:  It is defined by the PCS implementation
        whether one or more threads of control should be available to process
        incoming messages and to wait for their completion.

        21.b   Implementation Note:  At link-time, the linker provides the
        RPC-receiver and the necessary tables to support it.  A call on
        Establish_RPC_Receiver is inserted just before the call on the main
        subprogram.

        21.c   Reason:  The interface between the PCS (the System.RPC
        package) and the RPC-receiver is defined to be dynamic in order to
        allow the elaboration sequence to notify the PCS that all packages
        have been elaborated and that it is safe to call the receiving stubs.
        It is not guaranteed that the PCS units will be the last to be
        elaborated, so some other indication that elaboration is complete is
        needed.

22   If a call on Do_RPC is aborted, a cancellation message is sent to the
called partition, to request that the execution of the remotely called
subprogram be aborted.

        22.a   To be honest:  The full effects of this message are dependent
        on the implementation of the PCS.

23   {potentially blocking operation [RPC operations]} {blocking, potentially
[RPC operations]} The subprograms declared in System.RPC are potentially
blocking operations.  {94-4472.zj}


                         Implementation Requirements

24   The implementation of the RPC-receiver shall be reentrant[, thereby
allowing concurrent calls on it from the PCS to service concurrent remote
subprogram calls into the partition].

        24.a   Reason:  There seems no reason to allow the implementation of
        RPC-receiver to be nonreentrant, even though we don't require that
        every implementation of the PCS actually perform concurrent calls on
        the RPC-receiver.


                         Documentation Requirements

25   {documentation requirements} The implementation of the PCS shall
document whether the RPC-receiver is invoked from concurrent tasks.  If there
is an upper limit on the number of such tasks, this limit shall be documented
as well, together with the mechanisms to configure it (if this is supported).

        25.a   Implementation defined:  Implementation-defined aspects of the
        PCS.


                         Implementation Permissions

26   The PCS is allowed to contain implementation-defined interfaces for
explicit message passing, broadcasting, etc. Similarly, it is allowed to
provide additional interfaces to query the state of some remote partition
(given its partition ID) or of the PCS itself, to set timeouts and retry
parameters, to get more detailed error status, etc.  These additional
interfaces should be provided in child packages of System.RPC.

        26.a   Implementation defined:  Implementation-defined interfaces in
        the PCS.

27   A body for the package System.RPC need not be supplied by the
implementation.

        27.a   Reason:  It is presumed that a body for the package System.RPC
        might be extremely environment specific.  Therefore, we do not
        require that a body be provided by the (compiler) implementation.
        The user will have to write a body, or acquire one, appropriate for
        the target environment.


                            Implementation Advice

28   Whenever possible, the PCS on the called partition should allow for
multiple tasks to call the RPC-receiver with different messages and should
allow them to block until the corresponding subprogram body returns.
{94-4472.zk}

29   The Write operation on a stream of type Params_Stream_Type should raise
Storage_Error if it runs out of space trying to write the Item into the
stream.

        29.a   Implementation Note:  An implementation could also dynamically
        allocate more space as needed, only propagating Storage_Error if the
        allocator it calls raises Storage_Error.  This storage could be
        managed through a controlled component of the stream object, to
        ensure that it is reclaimed when the stream object is finalized.


     NOTES
30   (8) The package System.RPC is not designed for direct calls by user
     programs.  It is instead designed for use in the implementation of
     remote subprograms calls, being called by the calling stubs generated
     for a remote call interface library unit to initiate a remote call, and
     in turn calling back to an RPC-receiver that dispatches to the receiving
     stubs generated for the body of a remote call interface, to handle a
     remote call received from elsewhere.



                                   Annex F
                                 (normative)


                             Information Systems



1   {information systems} This Annex provides a set of facilities relevant to
Information Systems programming.  These fall into several categories:

    2  an attribute definition clause specifying Machine_Radix for a
       decimal subtype;

    3  the package Decimal, which declares a set of constants defining
       the implementation's capacity for decimal types, and a generic
       procedure for decimal division; and

    4  the child packages Text_IO.Editing and Wide_Text_IO.Editing,
       which support formatted and localized output of decimal data,
       based on ``picture String'' values.

5   See also: 3.5.9, ``Fixed Point Types''; 3.5.10, ``Operations of Fixed
Point Types''; 4.6, ``Type Conversions''; 13.3, ``Representation At-
tributes''; A.10.9, ``Input-Output for Real Types''; B.4, ``Interfacing with
COBOL''; B.3, ``Interfacing with C''; Annex G, ``Numerics''.

6   The character and string handling packages in Annex A, ``Predefined
Language Environment'' are also relevant for Information Systems.


                            Implementation Advice

7   If COBOL (respectively, C) is widely supported in the target environment,
implementations supporting the Information Systems Annex should provide the
child package Interfaces.COBOL (respectively, Interfaces.C) specified in
Annex B and should support a convention_identifier of COBOL (respectively, C)
in the interfacing pragmas (see Annex B), thus allowing Ada programs to
interface with programs written in that language.


                            Extensions to Ada 83

        7.a   {extensions to Ada 83} This Annex is new to Ada 9X.



F.1 Machine_Radix Attribute Definition Clause

                              Static Semantics

1   {specifiable [of Machine_Radix for decimal first subtypes]} {Machine_
Radix clause} Machine_Radix may be specified for a decimal first subtype (see
3.5.9) via an attribute_definition_clause; the expression of such a clause
shall be static, and its value shall be 2 or 10.  {94-4827.b} {94-4827.a} A
value of 2 implies a binary base range; a value of 10 implies a decimal base
range.

        1.a   Ramification:  In the absence of a Machine_Radix clause, the
        choice of 2 versus 10 for S'Machine_Radix is not specified.


                            Implementation Advice

2   Packed decimal should be used as the internal representation for objects
of subtype S when S'Machine_Radix = 10.


        2.a   Discussion:  The intent of a decimal Machine_Radix attribute
        definition clause is to allow the programmer to declare an Ada
        decimal data object whose representation matches a particular COBOL
        implementation's representation of packed decimal items.  The Ada
        object may then be passed to an interfaced COBOL program that takes a
        packed decimal data item as a parameter, assuming that convention
        COBOL has been specified for the Ada object's type in a pragma
        Convention.

        2.b   Additionally, the Ada compiler may choose to generate
        arithmetic instructions that exploit the packed decimal represen-
        tation.

                                  Examples

3   Example of Machine_Radix attribute definition clause:

4   type Money is delta 0.01 digits 15;
    for Money'Machine_Radix use 10;



F.2 The Package Decimal

                              Static Semantics

1   The library package Decimal has the following declaration:

2   package Ada.Decimal is
       pragma Pure(Decimal);

3      Max_Scale : constant := implementation-defined;
       Min_Scale : constant := implementation-defined;

4      Min_Delta : constant := 10.0**(-Max_Scale);
       Max_Delta : constant := 10.0**(-Min_Scale);

5      Max_Decimal_Digits : constant := implementation-defined;

6      generic
          type Dividend_Type  is delta <> digits <>;
          type Divisor_Type   is delta <> digits <>;
          type Quotient_Type  is delta <> digits <>;
          type Remainder_Type is delta <> digits <>;
       procedure Divide (Dividend  : in Dividend_Type;
                         Divisor   : in Divisor_Type;
                         Quotient  : out Quotient_Type;
                         Remainder : out Remainder_Type);
       pragma Convention(Intrinsic, Divide);

7   end Ada.Decimal;

        7.a   Implementation defined:  The values of named numbers in the
        package Decimal.

8   Max_Scale is the largest N such that 10.0**(-N) is allowed as a decimal
type's delta.  Its type is universal_integer.

9   Min_Scale is the smallest N such that 10.0**(-N) is allowed as a decimal
type's delta. Its type is universal_integer.

10   Min_Delta is the smallest value allowed for delta in a decimal_fixed_
point_definition.  Its type is universal_real.

11   Max_Delta is the largest value allowed for delta in a decimal_fixed_
point_definition.  Its type is universal_real.

12   Max_Decimal_Digits is the largest value allowed for digits in a decimal_
fixed_point_definition.  Its type is universal_integer.

        12.a   Reason:  The name is Max_Decimal_Digits versus Max_Digits, in
        order to avoid confusion with the named number System.Max_Digits
        relevant to floating point.
                              Static Semantics

13   The effect of Divide is as follows.  The value of Quotient is Quotient_
Type(Dividend/Divisor).  The value of Remainder is Remainder_
Type(Intermediate), where Intermediate is the difference between Dividend and
the product of Divisor and Quotient; this result is computed exactly.


                         Implementation Requirements

14   Decimal.Max_Decimal_Digits shall be at least 18.

15   Decimal.Max_Scale shall be at least 18.

16   Decimal.Min_Scale shall be at most 0.


     NOTES
17   (1) The effect of division yielding a quotient with control over
     rounding versus truncation is obtained by applying either the function
     attribute Quotient_Type'Round or the conversion Quotient_Type to the
     expression Dividend/Divisor.



F.3 Edited Output for Decimal Types

1   The child packages Text_IO.Editing and Wide_Text_IO.Editing provide
localizable formatted text output, known as edited output {edited output} ,
for decimal types.  An edited output string is a function of a numeric value,
program-specifiable locale elements, and a format control value.  The numeric
value is of some decimal type.  The locale elements are:

    2  the currency string;

    3  the digits group separator character;

    4  the radix mark character; and

    5  the fill character that replaces leading zeros of the numeric
       value.

6   For Text_IO.Editing the edited output and currency strings are of type
String, and the locale characters are of type Character.  For Wide_
Text_IO.Editing their types are Wide_String and Wide_Character, respectively.

7   Each of the locale elements has a default value that can be replaced or
explicitly overridden.

8   A format-control value is of the private type Picture; it determines the
composition of the edited output string and controls the form and placement
of the sign, the position of the locale elements and the decimal digits, the
presence or absence of a radix mark, suppression of leading zeros, and
insertion of particular character values.

9   A Picture object is composed from a String value, known as a picture
String, that serves as a template for the edited output string, and a Boolean
value that controls whether a string of all space characters is produced when
the number's value is zero.  A picture String comprises a sequence of one- or
two-Character symbols, each serving as a placeholder for a character or
string at a corresponding position in the edited output string.  The picture
String symbols fall into several categories based on their effect on the
edited output string:

10
         Decimal Digit:      '9'
         Radix Control:      '.'  'V'
         Sign Control:  '+'  '-'  '<'  '>'  "CR"                             "D\
B"
         Currency Control:   '$'  '#'
         Zero Suppression:   'Z'  '*'
         Simple Insertion:   '_'  'B'  '0'  '/'

11   The entries are not case-sensitive.  Mixed- or lower-case forms for "CR"
and "DB", and lower-case forms for 'V', 'Z', and 'B', have the same effect as
the upper-case symbols shown.

12   An occurrence of a '9' Character in the picture String represents a
decimal digit position in the edited output string.

13   A radix control Character in the picture String indicates the position
of the radix mark in the edited output string: an actual character position
for '.', or an assumed position for 'V'.

14   A sign control Character in the picture String affects the form of the
sign in the edited output string.  The '<' and '>' Character values indicate
parentheses for negative values.  A Character '+', '-', or '<' appears either
singly, signifying a fixed-position sign in the edited output, or repeated,
signifying a floating-position sign that is preceded by zero or more space
characters and that replaces a leading 0.

15   A currency control Character in the picture String indicates an
occurrence of the currency string in the edited output string.  The '$'
Character represents the complete currency string; the '#' Character
represents one character of the currency string.  A '$' Character appears
either singly, indicating a fixed-position currency string in the edited
output, or repeated, indicating a floating-position currency string that
occurs in place of a leading 0.  A sequence of '#' Character values indicates
either a fixed- or floating-position currency string, depending on context.

16   A zero suppression Character in the picture String allows a leading zero
to be replaced by either the space character (for 'Z') or the fill character
(for '*').

17   A simple insertion Character in the picture String represents, in
general, either itself (if '/' or '0'), the space character (if 'B'), or the
digits group separator character (if '_').  In some contexts it is treated as
part of a floating sign, floating currency, or zero suppression string.

18   An example of a picture String is "<###Z_ZZ9.99>".  If the currency
string is "FF", the separator character is ',', and the radix mark is '.'
then the edited output string values for the decimal values 32.10 and
-5432.10 are "bbFFbbb32.10b" and "(bFF5,432.10)", respectively, where 'b'
indicates the space character.

19   The generic packages Text_IO.Decimal_IO and Wide_Text_IO.Decimal_IO (see
A.10.9, ``Input-Output for Real Types'') provide text input and non-edited
text output for decimal types.


     NOTES
20   (2) A picture String is of type Standard.String, both for
     Text_IO.Editing and Wide_Text_IO.Editing.



F.3.1 Picture String Formation

1   {picture String (for edited output)} {well-formed picture String (for
edited output)} A well-formed picture String, or simply picture String, is a
String value that conforms to the syntactic rules, composition constraints,
and character replication conventions specified in this clause.


                              Dynamic Semantics

2

3   picture_string ::=
       fixed_$_picture_string
     | fixed_#_picture_string
     | floating_currency_picture_string
     | non_currency_picture_string


4   fixed_$_picture_string ::=
       [fixed_LHS_sign] fixed_$_char {direct_insertion} [zero_suppression]
         number [RHS_sign]

     | [fixed_LHS_sign {direct_insertion}] [zero_suppression]
         number fixed_$_char {direct_insertion} [RHS_sign]

     | floating_LHS_sign number fixed_$_char {direct_insertion} [RHS_sign]

     | [fixed_LHS_sign] fixed_$_char {direct_insertion}
         all_zero_suppression_number {direct_insertion}  [RHS_sign]

     | [fixed_LHS_sign {direct_insertion}] all_zero_suppression_number {direct_\
insertion}
         fixed_$_char {direct_insertion} [RHS_sign]

     | all_sign_number {direct_insertion} fixed_$_char {direct_insertion} [RHS_\
sign]


5   fixed_#_picture_string ::=
       [fixed_LHS_sign] single_#_currency {direct_insertion}
         [zero_suppression] number [RHS_sign]

     | [fixed_LHS_sign] multiple_#_currency {direct_insertion}
         zero_suppression number [RHS_sign]

     | [fixed_LHS_sign {direct_insertion}] [zero_suppression]
         number fixed_#_currency {direct_insertion} [RHS_sign]

     | floating_LHS_sign number fixed_#_currency {direct_insertion} [RHS_sign]

     | [fixed_LHS_sign] single_#_currency {direct_insertion}
         all_zero_suppression_number {direct_insertion} [RHS_sign]

     | [fixed_LHS_sign] multiple_#_currency {direct_insertion}
         all_zero_suppression_number {direct_insertion} [RHS_sign]

     | [fixed_LHS_sign {direct_insertion}] all_zero_suppression_number {direct_\
insertion}
         fixed_#_currency {direct_insertion} [RHS_sign]

     | all_sign_number {direct_insertion} fixed_#_currency {direct_insertion} [\
RHS_sign]


6   floating_currency_picture_string ::=
       [fixed_LHS_sign] {direct_insertion} floating_$_currency number [RHS_sign]
     | [fixed_LHS_sign] {direct_insertion} floating_#_currency number [RHS_sign]
     | [fixed_LHS_sign] {direct_insertion} all_currency_number {direct_insertio\
n} [RHS_sign]


7   non_currency_picture_string ::=
       [fixed_LHS_sign {direct_insertion}] zero_suppression number [RHS_sign]
     | [floating_LHS_sign] number [RHS_sign]
     | [fixed_LHS_sign {direct_insertion}] all_zero_suppression_number {direct_\
insertion} [RHS_sign]
     | all_sign_number {direct_insertion}
     | fixed_LHS_sign direct_insertion {direct_insertion} number [RHS_sign]
8   fixed_LHS_sign ::=  LHS_Sign

9   LHS_Sign ::=  + | - | <


10  fixed_$_char ::= $


11  direct_insertion ::=  simple_insertion

12  simple_insertion ::=  _ | B | 0 | /


13  zero_suppression ::=  Z {Z | context_sensitive_insertion} | fill_string

14  context_sensitive_insertion ::=  simple_insertion


15  fill_string ::=  * {* | context_sensitive_insertion}


16  number ::=
       fore_digits [radix [aft_digits] {direct_insertion}]
     | radix aft_digits {direct_insertion}

17  fore_digits ::= 9 {9 | direct_insertion}

18  aft_digits ::=  {9 | direct_insertion} 9

19  radix ::= . | V


20  RHS_sign ::= + | - | > | CR | DB


21  floating_LHS_sign ::=
       LHS_Sign {context_sensitive_insertion} LHS_Sign {LHS_Sign | context_sens\
itive_insertion}


22  single_#_currency ::= #

23  multiple_#_currency ::= ## {#}


24  fixed_#_currency ::= single_#_currency | multiple_#_currency


25  floating_$_currency ::=
       $ {context_sensitive_insertion} $ {$ | context_sensitive_insertion}


26  floating_#_currency ::=
       # {context_sensitive_insertion} # {# | context_sensitive_insertion}


27  all_sign_number ::=  all_sign_fore [radix [all_sign_aft]] [>]

28  all_sign_fore ::=
       sign_char {context_sensitive_insertion} sign_char {sign_char | context_s\
ensitive_insertion}

29  all_sign_aft ::= {all_sign_aft_char} sign_char

    all_sign_aft_char ::=  sign_char | context_sensitive_insertion

30  sign_char ::= + | - | <


31  all_currency_number ::=  all_currency_fore [radix [all_currency_aft]]

32  all_currency_fore ::=
       currency_char {context_sensitive_insertion}
         currency_char {currency_char | context_sensitive_insertion}

33  all_currency_aft ::= {all_currency_aft_char} currency_char

    all_currency_aft_char ::= currency_char | context_sensitive_insertion

34  currency_char ::= $ | #


35  all_zero_suppression_number ::=  all_zero_suppression_fore [ radix [all_zer\
o_suppression_aft]]

36  all_zero_suppression_fore ::=
       zero_suppression_char {zero_suppression_char | context_sensitive_inserti\
on}

37  all_zero_suppression_aft ::= {all_zero_suppression_aft_char} zero_suppressi\
on_char

    all_zero_suppression_aft_char ::=  zero_suppression_char | context_sensitiv\
e_insertion

38  zero_suppression_char ::= Z | *

{94-4985.e}

39   The following composition constraints apply to a picture String:

   40  A floating_LHS_sign does not have occurrences of different LHS_
       Sign Character values.

   41  If a picture String has '<' as fixed_LHS_sign, then it has '>' as
       RHS_sign.

   42  If a picture String has '<' in a floating_LHS_sign or in an all_
       sign_number, then it has an occurrence of '>'.  {94-4985.a}

   43  If a picture String has '+' or '-' as fixed_LHS_sign, in a
       floating_LHS_sign, or in an all_sign_number, then it has no RHS_
       sign.  {94-4974.a}

   44  An instance of all_sign_number does not have occurrences of
       different sign_char Character values.

   45  An instance of all_currency_number does not have occurrences of
       different currency_char Character values.

   46  An instance of all_zero_suppression_number does not have
       occurrences of different zero_suppression_char Character values,
       except for possible case differences between 'Z' and 'z'.

47   A replicable Character is a Character that, by the above rules, can
occur in two consecutive positions in a picture String.

48   A Character replication is a String

49  char & '(' & spaces & count_string & ')'

50   where char is a replicable Character, spaces is a String (possibly
empty) comprising only space Character values, and count_string is a String
of one or more decimal digit Character values.  A Character replication in a
picture String has the same effect as (and is said to be equivalent to) a
String comprising n consecutive occurrences of char, where
n=Integer'Value(count_string).

51   An expanded picture String is a picture String containing no Character
replications.

        51.a   Discussion:  Since 'B' is not allowed after a RHS sign, there
        is no need for a special rule to disallow "9.99DB(2)" as an
        abbreviation for "9.99DBB"


     NOTES
52   (3) Although a sign to the left of the number can float, a sign to the
     right of the number is in a fixed position.



F.3.2 Edited Output Generation

                              Dynamic Semantics

1   The contents of an edited output string are based on:

    2  A value, Item, of some decimal type Num,

    3  An expanded picture String Pic_String,

    4  A Boolean value, Blank_When_Zero, {94-4985.f}

    5  A Currency string,

    6  A Fill character,

    7  A Separator character, and

    8  A Radix_Mark character.

9   The combination of a True value for Blank_When_Zero and a '*' character
in Pic_String is inconsistent; no edited output string is defined.

10   A layout error is identified in the rules below if leading non-zero
digits of Item, character values of the Currency string, or a negative sign
would be truncated; in such cases no edited output string is defined.
{94-4985.b}

11   The edited output string has lower bound 1 and upper bound N where N =
Pic_String'Length + Currency_Length_Adjustment - Radix_Adjustment, and

   12  Currency_Length_Adjustment = Currency'Length - 1 if there is some
       occurrence of '$' in Pic_String, and 0 otherwise.

   13  Radix_Adjustment = 1 if there is an occurrence of 'V' or 'v' in
       Pic_Str, and 0 otherwise.

14   {displayed magnitude (of a decimal value)} Let the magnitude of Item be
expressed as a base-10 number I ***I .F ***F , called the displayed magnitude
                               p    1  1    q
of Item, where:

   15  q = Min(Max(Num'Scale, 0), n) where n is 0 if Pic_String has no
       radix and is otherwise the number of digit positions following
       radix in Pic_String, where a digit position corresponds to an
       occurrence of '9', a zero_suppression_char (for an all_zero_
       suppression_number), a currency_char (for an all_currency_
       number), or a sign_char (for an all_sign_number).

   16  I  /= 0 if p>0.
        p
{94-4985.d}

17   If n < Num'Scale, then the above number is the result of rounding (away
from 0 if exactly midway between values).

18   If Blank_When_Zero = True and the displayed magnitude of Item is zero,
then the edited output string comprises all space character values.
Otherwise, the picture String is treated as a sequence of instances of
syntactic categories based on the rules in F.3.1, and the edited output
string is the concatenation of string values derived from these categories
according to the following mapping rules.

19   Table F-1 shows the mapping from a sign control symbol to a
corresponding character or string in the edited output.  In the columns
showing the edited output, a lower-case 'b' represents the space character.
If there is no sign control symbol but the value of Item is negative, a
layout error occurs and no edited output string is produced.  {94-4985.b}

      -----------------------------------------------------------------
      |                                                               |
      |       Table F-1: Edited Output for Sign Control Symbols       |
      |                                                               |
      |-------------------------------------------------------------- |
      |                     |                     |                   |
      |                     |  Edited Output for  | Edited Output for |
      | Sign Control Symbol | Non-Negative Number |  Negative Number  |
      |                     |                     |                   |
      |---------------------------------------------------------------|
      |                     |                     |                   |
      |         '+'         |         '+'         |        '-'        |
      |                     |                     |                   |
      |         '-'         |         'b'         |        '-'        |
      |                     |                     |                   |
      |         '<'         |         'b'         |        '('        |
      |                     |                     |                   |
      |         '>'         |         'b'         |        ')'        |
      |                     |                     |                   |
      |        "CR"         |        "bb"         |       "CR"        |
      |                     |                     |                   |
      |        "DB"         |        "bb"         |       "DB"        |
      |                     |                     |                   |
      -----------------------------------------------------------------

20   An instance of fixed_LHS_sign maps to a character as shown in Table F-1.

21   An instance of fixed_$_char maps to Currency.

22   An instance of direct_insertion maps to Separator if direct_insertion =
'_', and to the direct_insertion Character otherwise.

23   An instance of number maps to a string integer_part & radix_part &
fraction_part where:

   24  The string for integer_part is obtained as follows:

          25  Occurrences of '9' in fore_digits of number are replaced
              from right to left with the decimal digit character values
              for I , ..., I , respectively.
                   1        p
          26  Each occurrence of '9' in fore_digits to the left of the
              leftmost '9' replaced according to rule 1 is replaced with
              '0'.

          27  If p exceeds the number of occurrences of '9' in fore_
              digits of number, then the excess leftmost digits are
              eligible for use in the mapping of an instance of zero_
              suppression, floating_LHS_sign, floating_$_currency, or
              floating_#_currency to the left of number; if there is no
              such instance, then a layout error occurs and no edited
              output string is produced.

   28  The radix_part is:

          29  "" if number does not include a radix, if radix = 'V', or
              if radix = 'v'

          30  Radix_Mark if number includes '.' as radix

   31  The string for fraction_part is obtained as follows:

          32  Occurrences of '9' in aft_digits of number are replaced
              from left to right with the decimal digit character values
              for F , ... F .
                   1       q
          33  Each occurrence of '9' in aft_digits to the right of the
              rightmost '9' replaced according to rule 1 is replaced by
              '0'.

34   An instance of zero_suppression maps to the string obtained as follows:

   35  The rightmost 'Z', 'z', or '*' Character values are replaced with
       the excess digits (if any) from the integer_part of the mapping
       of the number to the right of the zero_suppression instance,

   36  A context_sensitive_insertion Character is replaced as though it
       were a direct_insertion Character, if it occurs to the right of
       some 'Z', 'z', or '*' in zero_suppression that has been mapped to
       an excess digit,

   37  Each Character to the left of the leftmost Character replaced
       according to rule 1 above is replaced by:

          38  the space character if the zero suppression Character is
              'Z' or 'z', or

          39  the Fill character if the zero suppression Character is
              '*'.

   40  A layout error occurs if some excess digits remain after all 'Z',
       'z', and '*' Character values in zero_suppression have been
       replaced via rule 1; no edited output string is produced.

41   An instance of RHS_sign maps to a character or string as shown in Table
F-1.

42   An instance of floating_LHS_sign maps to the string obtained as follows.

   43  Up to all but one of the rightmost LHS_Sign Character values are
       replaced by the excess digits (if any) from the integer_part of
       the mapping of the number to the right of the floating_LHS_sign
       instance.

   44  The next Character to the left is replaced with the character
       given by the entry in Table F-1 corresponding to the LHS_Sign
       Character.

   45  A context_sensitive_insertion Character is replaced as though it
       were a direct_insertion Character, if it occurs to the right of
       the leftmost LHS_Sign character replaced according to rule 1.

   46  Any other Character is replaced by the space character..

   47  A layout error occurs if some excess digits remain after
       replacement via rule 1; no edited output string is produced.

48   An instance of fixed_#_currency maps to the Currency string with n space
character values concatenated on the left (if the instance does not follow a
radix) or on the right (if the instance does follow a radix), where n is the
difference between the length of the fixed_#_currency instance and
Currency'Length.  A layout error occurs if Currency'Length exceeds the length
of the fixed_#_currency instance; no edited output string is produced.

49   An instance of floating_$_currency maps to the string obtained as
follows:

   50  Up to all but one of the rightmost '$' Character values are
       replaced with the excess digits (if any) from the integer_part of
       the mapping of the number to the right of the floating_$_currency
       instance.

   51  The next Character to the left is replaced by the Currency
       string.

   52  A context_sensitive_insertion Character is replaced as though it
       were a direct_insertion Character, if it occurs to the right of
       the leftmost '$' Character replaced via rule 1.

   53  Each other Character is replaced by the space character.

   54  A layout error occurs if some excess digits remain after
       replacement by rule 1; no edited output string is produced.

55   An instance of floating_#_currency maps to the string obtained as
follows:

   56  Up to all but one of the rightmost '#' Character values are
       replaced with the excess digits (if any) from the integer_part of
       the mapping of the number to the right of the floating_#_currency
       instance.  {94-4979.b}

   57  The substring whose last Character occurs at the position
       immediately preceding the leftmost Character replaced via rule 1,
       and whose length is Currency'Length, is replaced by the Currency
       string.  {94-4979.a}

   58  A context_sensitive_insertion Character is replaced as though it
       were a direct_insertion Character, if it occurs to the right of
       the leftmost '#' replaced via rule 1.

   59  Any other Character is replaced by the space character.

   60  A layout error occurs if some excess digits remain after
       replacement rule 1, or if there is no substring with the required
       length for replacement rule 2; no edited output string is
       produced.

61   An instance of all_zero_suppression_number maps to:

   62  a string of all spaces if the displayed magnitude of Item is
       zero, the zero_suppression_char is 'Z' or 'z', and the instance
       of all_zero_suppression_number does not have a radix at its last
       character position;

   63  a string containing the Fill character in each position except
       for the character (if any) corresponding to radix, if zero_
       suppression_char = '*' and the displayed magnitude of Item is
       zero;

   64  otherwise, the same result as if each zero_suppression_char in
       all_zero_suppression_aft were '9', interpreting the instance of
       all_zero_suppression_number as either zero_suppression number (if
       a radix and all_zero_suppression_aft are present), or as zero_
       suppression otherwise.

{94-4985.e}

65   An instance of all_sign_number maps to:

   66  a string of all spaces if the displayed magnitude of Item is zero
       and the instance of all_sign_number does not have a radix at its
       last character position;

   67  otherwise, the same result as if each sign_char in all_sign_
       number_aft were '9', interpreting the instance of all_sign_number
       as either floating_LHS_sign number (if a radix and all_sign_
       number_aft are present), or as floating_LHS_sign otherwise.

{94-4985.e}

68   An instance of all_currency_number maps to:

   69  a string of all spaces if the displayed magnitude of Item is zero
       and the instance of all_currency_number does not have a radix at
       its last character position;

   70  otherwise, the same result as if each currency_char in all_
       currency_number_aft were '9', interpreting the instance of all_
       currency_number as floating_$_currency number or
       floating_#_currency number (if a radix and all_currency_number_
       aft are present), or as floating_$_currency or
       floating_#_currency otherwise.

{94-4985.e}


                                  Examples

71   In the result string values shown below, 'b' represents the space
character.

72  Item:         Picture and Result Strings:

73  123456.78     Picture:  "-###**_***_**9.99"
                            "bbb$***123,456.78"
                            "bbFF***123.456,78" (currency = "FF",
                                                 separator = '.',
                                                 radix mark = ',')

74  123456.78     Picture:  "-$$$**_***_**9.99"
                  Result:   "bbb$***123,456.78"
                           "bbbFF***123.456,78" (currency = "FF",
                                                 separator = '.',
                                                 radix mark = ',')

75  0.0          Picture: "-$$$$$$.$$"
                 Result:  "bbbbbbbbbb"

76  0.20         Picture: "-$$$$$$.$$"
                 Result:  "bbbbbb$.20"

77  -1234.565    Picture: "<<<<_<<<.<<###>"
                 Result:  "bb(1,234.57DMb)"  (currency = "DM")

78  12345.67     Picture: "###_###_##9.99"
                 Result:  "bbCHF12,345.67"   (currency = "CHF")



F.3.3 The Package Text_IO.Editing

1   The package Text_IO.Editing provides a private type Picture with
associated operations, and a generic package Decimal_Output.  An object of
type Picture is composed from a well-formed picture String (see F.3.1) and a
Boolean item indicating whether a zero numeric value will result in an edited
output string of all space characters.  The package Decimal_Output contains
edited output subprograms implementing the effects defined in F.3.2.


                              Static Semantics

2   The library package Text_IO.Editing has the following declaration:

3   package Ada.Text_IO.Editing is

4      type Picture is private;


5      function Valid (Pic_String      : in String;
                       Blank_When_Zero : in Boolean := False) return Boolean;

6      function To_Picture (Pic_String      : in String;
                            Blank_When_Zero : in Boolean := False)
          return Picture;

7      function Pic_String      (Pic : in Picture) return String;
       function Blank_When_Zero (Pic : in Picture) return Boolean;

8      Max_Picture_Length  : constant := implementation_defined;

9      Picture_Error       : exception;

10     Default_Currency    : constant String    := "$";
       Default_Fill        : constant Character := '*';
       Default_Separator   : constant Character := ',';
       Default_Radix_Mark  : constant Character := '.';

11     generic
          type Num is delta <> digits <>;
          Default_Currency   : in String    :=  Text_IO.Editing.Default_Currenc\
y;
          Default_Fill       : in Character :=  Text_IO.Editing.Default_Fill;
          Default_Separator  : in Character :=  Text_IO.Editing.Default_Separat\
or;
          Default_Radix_Mark : in Character :=  Text_IO.Editing.Default_Radix_M\
ark;
       package Decimal_Output is
          function Length (Pic      : in Picture;
                           Currency : in String := Default_Currency)
             return Natural;

12        function Valid (Item     : in Num;
                          Pic      : in Picture;
                          Currency : in String := Default_Currency)
             return Boolean;

13        function Image (Item       : in Num;
                          Pic        : in Picture;
                          Currency   : in String    := Default_Currency;
                          Fill       : in Character := Default_Fill;
                          Separator  : in Character := Default_Separator;
                          Radix_Mark : in Character := Default_Radix_Mark)
             return String;

14        procedure Put (File       : in File_Type;
                         Item       : in Num;
                         Pic        : in Picture;
                         Currency   : in String    := Default_Currency;
                         Fill       : in Character := Default_Fill;
                         Separator  : in Character := Default_Separator;
                         Radix_Mark : in Character := Default_Radix_Mark);

15        procedure Put (Item       : in Num;
                         Pic        : in Picture;
                         Currency   : in String    := Default_Currency;
                         Fill       : in Character := Default_Fill;
                         Separator  : in Character := Default_Separator;
                         Radix_Mark : in Character := Default_Radix_Mark);

16        procedure Put (To         : out String;
                         Item       : in Num;
                         Pic        : in Picture;
                         Currency   : in String    := Default_Currency;
                         Fill       : in Character := Default_Fill;
                         Separator  : in Character := Default_Separator;
                         Radix_Mark : in Character := Default_Radix_Mark);
       end Decimal_Output;
    private
       ... -- not specified by the language
    end Ada.Text_IO.Editing;

{94-4480.f}

        16.a   Implementation defined:  The value of Max_Picture_Length in
        the package Text_IO.Editing

17   The exception Constraint_Error is raised if the Image function or any of
the Put procedures is invoked with a null string for Currency.  {94-4985.c}


18  function Valid (Pic_String      : in String;
                    Blank_When_Zero : in Boolean := False) return Boolean;

        19   Valid returns True if Pic_String is a well-formed picture String
        (see F.3.1) the length of whose expansion does not exceed Max_
        Picture_Length, and if either Blank_When_Zero is False or Pic_String
        contains no '*'.


20  function To_Picture (Pic_String      : in String;
                         Blank_When_Zero : in Boolean := False)
       return Picture;

        21   To_Picture returns a result Picture such that the application of
        the function Pic_String to this result yields an expanded picture
        String equivalent to Pic_String, and such that Blank_When_Zero
        applied to the result Picture is the same value as the parameter
        Blank_When_Zero.  Picture_Error is raised if not Valid(Pic_String,
        Blank_When_Zero).


22  function Pic_String      (Pic : in Picture) return String;

    function Blank_When_Zero (Pic : in Picture) return Boolean;

        23   If Pic is To_Picture(String_Item, Boolean_Item) for some String_
        Item and Boolean_Item, then:

           24  Pic_String(Pic) returns an expanded picture String
               equivalent to String_Item and with any lower-case letter
               replaced with its corresponding upper-case form, and

           25  Blank_When_Zero(Pic) returns Boolean_Item.
        26   If Pic_1 and Pic_2 are objects of type Picture, then "="(Pic_1,
        Pic_2) is True when

           27  Pic_String(Pic_1) = Pic_String(Pic_2), and

           28  Blank_When_Zero(Pic_1) = Blank_When_Zero(Pic_2).


29  function Length (Pic      : in Picture;
                     Currency : in String := Default_Currency)
       return Natural;

        30   Length returns Pic_String(Pic)'Length + Currency_Length_
        Adjustment - Radix_Adjustment where

           31  Currency_Length_Adjustment =

                  32  Currency'Length - 1 if there is some occurrence of
                      '$' in Pic_String(Pic), and

                  33  0 otherwise.

           34  Radix_Adjustment =

                  35  1 if there is an occurrence of 'V' or 'v' in Pic_
                      Str(Pic), and

                  36  0 otherwise.


37  function Valid (Item     : in Num;
                    Pic      : in Picture;
                    Currency : in String := Default_Currency)
       return Boolean;

        38   Valid returns True if Image(Item, Pic, Currency) does not raise
        Layout_Error, and returns False otherwise.


39  function Image (Item       : in Num;
                    Pic        : in Picture;
                    Currency   : in String    := Default_Currency;
                    Fill       : in Character := Default_Fill;
                    Separator  : in Character := Default_Separator;
                    Radix_Mark : in Character := Default_Radix_Mark)
       return String;

        40   Image returns the edited output String as defined in F.3.2 for
        Item, Pic_String(Pic), Blank_When_Zero(Pic), Currency, Fill,
        Separator, and Radix_Mark.  If these rules identify a layout error,
        then Image raises the exception Layout_Error.


41  procedure Put (File       : in File_Type;
                   Item       : in Num;
                   Pic        : in Picture;
                   Currency   : in String    := Default_Currency;
                   Fill       : in Character := Default_Fill;
                   Separator  : in Character := Default_Separator;
                   Radix_Mark : in Character := Default_Radix_Mark);

    procedure Put (Item       : in Num;
                   Pic        : in Picture;
                   Currency   : in String    := Default_Currency;
                   Fill       : in Character := Default_Fill;
                   Separator  : in Character := Default_Separator;
                   Radix_Mark : in Character := Default_Radix_Mark);

        42   Each of these Put procedures outputs Image(Item, Pic, Currency,
        Fill, Separator, Radix_Mark) consistent with the conventions for Put
        for other real types in case of bounded line length (see A.10.6,
        ``Get and Put Procedures'').


43  procedure Put (To         : out String;
                   Item       : in Num;
                   Pic        : in Picture;
                   Currency   : in String    := Default_Currency;
                   Fill       : in Character := Default_Fill;
                   Separator  : in Character := Default_Separator;
                   Radix_Mark : in Character := Default_Radix_Mark);

        44   Put copies Image(Item, Pic, Currency, Fill, Separator, Radix_
        Mark) to the given string, right justified.  Otherwise unassigned
        Character values in To are assigned the space character.  If
        To'Length is less than the length of the string resulting from Image,
        then Layout_Error is raised.


                         Implementation Requirements

45   Max_Picture_Length shall be at least 30.  The implementation shall
support currency strings of length up to at least 10, both for Default_
Currency in an instantiation of Decimal_Output, and for Currency in an
invocation of Image or any of the Put procedures.  {94-4480.f}

        45.a   Discussion:  This implies that a picture string with character
        replications need not be supported (i.e., To_Picture will raise
        Picture_Error) if its expanded form exceeds 30 characters.


     NOTES
46   (4) The rules for edited output are based on COBOL (ANSI X3.23:1985,
     endorsed by ISO as ISO 1989-1985), with the following differences:

        47  The COBOL provisions for picture string localization and for
            'P' format are absent from Ada.

        48  The following Ada facilities are not in COBOL:

               49  currency symbol placement after the number,

               50  localization of edited output string for multi-
                   character currency string values, including support
                   for both length-preserving and length-expanding
                   currency symbols in picture strings

               51  localization of the radix mark, digits separator, and
                   fill character, and

               52  parenthesization of negative values.

     The value of 30 for Max_Picture_Length is the same limit as in COBOL.


        52.a   Reason:  There are several reasons we have not adopted the
        COBOL-style permission to provide a single-character replacement in
        the picture string for the `$' as currency symbol, or to interchange
        the roles of `.' and `,' in picture strings

         52.b  It would have introduced considerable complexity into
               Ada, as well as confusion between run-time and
               compile-time character interpretation, since picture
               Strings are dynamically computable in Ada, in contrast
               with COBOL

         52.c  Ada's rules for real literals provide a natural
               interpretation of `_' as digits separator and `.' for
               radix mark; it is not essential to allow these to be
               localized in picture strings, since Ada does not allow
               them to be localized in real literals.

         52.d  The COBOL restriction for the currency symbol in a
               picture string to be replaced by a single character
               currency symbol is a compromise solution.  For general
               international usage a mechanism is needed to localize the
               edited output to be a multi-character currency string.
               Allowing a single-Character localization for the picture
               Character, and a multiple-character localization for the
               currency string, would be an unnecessary complication.



F.3.4 The Package Wide_Text_IO.Editing

                              Static Semantics

1   {Ada.Wide_Text_IO.Editing} The child package Wide_Text_IO.Editing has the
same contents as Text_IO.Editing, except that:

    2  each occurrence of Character is replaced by Wide_Character,

    3  each occurrence of Text_IO is replaced by Wide_Text_IO,

    4  the subtype of Default_Currency is Wide_String rather than
       String, and

    5  each occurrence of String in the generic package Decimal_Output
       is replaced by Wide_String.

        5.a   Implementation defined:  The value of Max_Picture_Length in the
        package Wide_Text_IO.Editing


     NOTES
6    (5) Each of the functions Wide_Text_IO.Editing.Valid, To_Picture, and
     Pic_String has String (versus Wide_String) as its parameter or result
     subtype, since a picture String is not localizable.



                                   Annex G
                                 (normative)


                                   Numerics



1   {numerics} The Numerics Annex specifies

    2  features for complex arithmetic, including complex I/O;

    3  a mode (``strict mode''), in which the predefined arithmetic
       operations of floating point and fixed point types and the
       functions and operations of various predefined packages have to
       provide guaranteed accuracy or conform to other numeric
       performance requirements, which the Numerics Annex also
       specifies;

    4  a mode (``relaxed mode''), in which no accuracy or other numeric
       performance requirements need be satisfied, as for implemen-
       tations not conforming to the Numerics Annex;

    5  models of floating point and fixed point arithmetic on which the
       accuracy requirements of strict mode are based; and

    6  the definitions of the model-oriented attributes of floating
       point types that apply in the strict mode.


                            Implementation Advice

7   If Fortran (respectively, C) is widely supported in the target
environment, implementations supporting the Numerics Annex should provide the
child package Interfaces.Fortran (respectively, Interfaces.C) specified in
Annex B and should support a convention_identifier of Fortran (respectively,
C) in the interfacing pragmas (see Annex B), thus allowing Ada programs to
interface with programs written in that language.


                            Extensions to Ada 83

        7.a   {extensions to Ada 83} This Annex is new to Ada 9X.



G.1 Complex Arithmetic

1   Types and arithmetic operations for complex arithmetic are provided in
Generic_Complex_Types, which is defined in G.1.1.  Implementation-defined
approximations to the complex analogs of the mathematical functions known as
the ``elementary functions'' are provided by the subprograms in Generic_
Complex_Elementary_Functions, which is defined in G.1.2.  Both of these
library units are generic children of the predefined package Numerics (see
A.5).  Nongeneric equivalents of these generic packages for each of the
predefined floating point types are also provided as children of Numerics.

        1.a   Implementation defined:  The accuracy actually achieved by the
        complex elementary functions and by other complex arithmetic
        operations.

        1.b   Discussion:  Complex arithmetic is defined in the Numerics
        Annex, rather than in the core, because it is considered to be a
        specialized need of (some) numeric applications.



G.1.1 Complex Types

                              Static Semantics

1   The generic library package Numerics.Generic_Complex_Types has the
following declaration:

2   generic
       type Real is digits <>;
    package Ada.Numerics.Generic_Complex_Types is
       pragma Pure(Generic_Complex_Types);

3      type Complex is
          record
             Re, Im : Real'Base;
          end record;

4      type Imaginary is private;

5      i : constant Imaginary;
       j : constant Imaginary;

6      function Re (X : Complex)   return Real'Base;
       function Im (X : Complex)   return Real'Base;
       function Im (X : Imaginary) return Real'Base;

7      procedure Set_Re (X  : in out Complex;
                         Re : in     Real'Base);
       procedure Set_Im (X  : in out Complex;
                         Im : in     Real'Base);
       procedure Set_Im (X  :    out Imaginary;
                         Im : in     Real'Base);

8      function Compose_From_Cartesian (Re, Im : Real'Base) return Complex;
       function Compose_From_Cartesian (Re     : Real'Base) return Complex;
       function Compose_From_Cartesian (Im     : Imaginary) return Complex;

9      function Modulus (X     : Complex) return Real'Base;
       function "abs"   (Right : Complex) return Real'Base renames Modulus;

10     function Argument (X     : Complex)   return Real'Base;
       function Argument (X     : Complex;
                          Cycle : Real'Base) return Real'Base;

11     function Compose_From_Polar (Modulus, Argument        : Real'Base)
          return Complex;
       function Compose_From_Polar (Modulus, Argument, Cycle : Real'Base)
          return Complex;

12     function "+"       (Right : Complex) return Complex;
       function "-"       (Right : Complex) return Complex;
       function Conjugate (X     : Complex) return Complex;

13     function "+" (Left, Right : Complex) return Complex;
       function "-" (Left, Right : Complex) return Complex;
       function "*" (Left, Right : Complex) return Complex;
       function "/" (Left, Right : Complex) return Complex;

14     function "**" (Left : Complex; Right : Integer) return Complex;

15     function "+"       (Right : Imaginary) return Imaginary;
       function "-"       (Right : Imaginary) return Imaginary;
       function Conjugate (X     : Imaginary) return Imaginary renames "-";
       function "abs"     (Right : Imaginary) return Real'Base;

16     function "+" (Left, Right : Imaginary) return Imaginary;
       function "-" (Left, Right : Imaginary) return Imaginary;
       function "*" (Left, Right : Imaginary) return Real'Base;
       function "/" (Left, Right : Imaginary) return Real'Base;

17     function "**" (Left : Imaginary; Right : Integer) return Complex;

18     function "<"  (Left, Right : Imaginary) return Boolean;
       function "<=" (Left, Right : Imaginary) return Boolean;
       function ">"  (Left, Right : Imaginary) return Boolean;
       function ">=" (Left, Right : Imaginary) return Boolean;

19     function "+" (Left : Complex;   Right : Real'Base) return Complex;
       function "+" (Left : Real'Base; Right : Complex)   return Complex;
       function "-" (Left : Complex;   Right : Real'Base) return Complex;
       function "-" (Left : Real'Base; Right : Complex)   return Complex;
       function "*" (Left : Complex;   Right : Real'Base) return Complex;
       function "*" (Left : Real'Base; Right : Complex)   return Complex;
       function "/" (Left : Complex;   Right : Real'Base) return Complex;
       function "/" (Left : Real'Base; Right : Complex)   return Complex;

20     function "+" (Left : Complex;   Right : Imaginary) return Complex;
       function "+" (Left : Imaginary; Right : Complex)   return Complex;
       function "-" (Left : Complex;   Right : Imaginary) return Complex;
       function "-" (Left : Imaginary; Right : Complex)   return Complex;
       function "*" (Left : Complex;   Right : Imaginary) return Complex;
       function "*" (Left : Imaginary; Right : Complex)   return Complex;
       function "/" (Left : Complex;   Right : Imaginary) return Complex;
       function "/" (Left : Imaginary; Right : Complex)   return Complex;

21     function "+" (Left : Imaginary; Right : Real'Base) return Complex;
       function "+" (Left : Real'Base; Right : Imaginary) return Complex;
       function "-" (Left : Imaginary; Right : Real'Base) return Complex;
       function "-" (Left : Real'Base; Right : Imaginary) return Complex;
       function "*" (Left : Imaginary; Right : Real'Base) return Imaginary;
       function "*" (Left : Real'Base; Right : Imaginary) return Imaginary;
       function "/" (Left : Imaginary; Right : Real'Base) return Imaginary;
       function "/" (Left : Real'Base; Right : Imaginary) return Imaginary;

22  private

23     type Imaginary is new Real'Base;
       i : constant Imaginary := 1.0;
       j : constant Imaginary := 1.0;

24  end Ada.Numerics.Generic_Complex_Types;

25   {Ada.Numerics.Complex_Types} The library package Numerics.Complex_Types
defines the same types, constants, and subprograms as Numerics.Generic_
Complex_Types, except that the predefined type Float is systematically
substituted for Real'Base throughout.  Nongeneric equivalents of
Numerics.Generic_Complex_Types for each of the other predefined floating
point types are defined similarly, with the names Numerics.Short_Complex_
Types, Numerics.Long_Complex_Types, etc.

        25.a   Reason:  The nongeneric equivalents are provided to allow the
        programmer to construct simple mathematical applications without
        being required to understand and use generics.

        25.b   Reason:  The nongeneric equivalents all export the types
        Complex and Imaginary and the constants i and j (rather than uniquely
        named types and constants, such as Short_Complex, Long_Complex, etc.)
        to preserve their equivalence to actual instantiations of the generic
        package and to allow the programmer to change the precision of an
        application globally by changing a single context clause.

26   [Complex is a visible type with cartesian components.]

        26.a   Reason:  The cartesian representation is far more common than
        the polar representation, in practice.  The accuracy of the results
        of the complex arithmetic operations and of the complex elementary
        functions is dependent on the representation; thus, implementers need
        to know that representation.  The type is visible so that complex
        ``literals'' can be written in aggregate notation, if desired.

27   [Imaginary is a private type; its full type is derived from Real'Base.]

        27.a   Reason:  The Imaginary type and the constants i and j are
        provided for two reasons:

         27.b  They allow complex ``literals'' to be written in the
               alternate form of a + b*i (or a + b*j), if desired.  Of
               course, in some contexts the sum will need to be
               parenthesized.

         27.c  When an Ada binding to IEC 559:1989 that provides
               (signed) infinities as the result of operations that
               overflow becomes available, it will be important to allow
               arithmetic between pure-imaginary and complex operands
               without requiring the former to be represented as (or
               promoted to) complex values with a real component of
               zero.  For example, the multiplication of a + b*i by d*i
               should yield -b*d + a*d*i, but if one cannot avoid
               representing the pure-imaginary value d*i as the complex
               value 0.0 + d*i, then a NaN ("Not-a-Number") could be
               produced as the result of multiplying a by 0.0 (e.g.,
               when a is infinite); the NaN could later trigger an
               exception.  Providing the Imaginary type and overloadings
               of the arithmetic operators for mixtures of Imaginary and
               Complex operands gives the programmer the same control
               over avoiding premature coercion of pure-imaginary values
               to complex as is already provided for pure-real values.

        27.d   Reason:  The Imaginary type is private, rather than being
        visibly derived from Real'Base, for two reasons:

         27.e  to preclude implicit conversions of real literals to the
               Imaginary type (such implicit conversions would make many
               common arithmetic expressions ambiguous); and

         27.f  to suppress the implicit derivation of the multiplica-
               tion, division, and absolute value operators with
               Imaginary operands and an Imaginary result (the result
               type would be incorrect).

        27.g   Reason:  The base subtype Real'Base is used for the component
        type of Complex, the parent type of Imaginary, and the parameter and
        result types of some of the subprograms to maximize the chances of
        being able to pass meaningful values into the subprograms and receive
        meaningful results back.  The generic formal parameter Real therefore
        plays only one role, that of providing the precision to be maintained
        in complex arithmetic calculations.  Thus, the subprograms in
        Numerics.Generic_Complex_Types share with those in Numerics.Generic_
        Elementary_Functions, and indeed even with the predefined arithmetic
        operations (see 4.5), the property of being free of range checks on
        input and output, i.e., of being able to exploit the base range of
        the relevant floating point type fully.  As a result, the user loses
        the ability to impose application-oriented bounds on the range of
        values that the components of a complex variable can acquire;
        however, it can be argued that few, if any, applications have a
        naturally square domain (as opposed to a circular domain) anyway.

28   The arithmetic operations and the Re, Im, Modulus, Argument, and
Conjugate functions have their usual mathematical meanings.  When applied to
a parameter of pure-imaginary type, the ``imaginary-part'' function Im yields
the value of its parameter, as the corresponding real value.

        28.a   Reason:  The latter case can be understood by considering the
        parameter of pure-imaginary type to represent a complex value with a
        zero real part.

The remaining subprograms have the following meanings:

   29  The Set_Re and Set_Im procedures replace the designated component
       of a complex parameter with the given real value; applied to a
       parameter of pure-imaginary type, the Set_Im procedure replaces
       the value of that parameter with the imaginary value
       corresponding to the given real value.

   30  The Compose_From_Cartesian function constructs a complex value
       from the given real and imaginary components.  If only one
       component is given, the other component is implicitly zero.

   31  The Compose_From_Polar function constructs a complex value from
       the given modulus (radius) and argument (angle).  When the value
       of the parameter Modulus is positive (resp., negative), the
       result is the complex value represented by the point in the
       complex plane lying at a distance from the origin given by the
       absolute value of Modulus and forming an angle measured
       counterclockwise from the positive (resp., negative) real axis
       given by the value of the parameter Argument.

32   When the Cycle parameter is specified, the result of the Argument
function and the parameter Argument of the Compose_From_Polar function are
measured in units such that a full cycle of revolution has the given value;
otherwise, they are measured in radians.

33   The computed results of the mathematically multivalued functions are
rendered single-valued by the following conventions, which are meant to imply
the principal branch:

   34  The result of the Modulus function is nonnegative.

   35  The result of the Argument function is in the quadrant containing
       the point in the complex plane represented by the parameter
       X. This may be any quadrant (I through IV); thus, the range of
       the Argument function is approximately -Pi to Pi (-Cycle/2.0 to
       Cycle/2.0, if the parameter Cycle is specified).  When the point
       represented by the parameter X lies on the negative real axis,
       the result approximates

          36  Pi (resp., -Pi) when the sign of the imaginary component
              of X is positive (resp., negative), if Real'Signed_Zeros
              is True;

          37  Pi, if Real'Signed_Zeros is False.

   38  Because a result lying on or near one of the axes may not be
       exactly representable, the approximation inherent in computing
       the result may place it in an adjacent quadrant, close to but on
       the wrong side of the axis.


                              Dynamic Semantics

39   The exception Numerics.Argument_Error is raised by the Argument and
Compose_From_Polar functions with specified cycle, signaling a parameter
value outside the domain of the corresponding mathematical function, when the
value of the parameter Cycle is zero or negative.

40   {Division_Check [partial]} {check, language-defined (Division_Check)}
{Constraint_Error (raised by failure of run-time check)} The exception
Constraint_Error is raised by the division operator when the value of the
right operand is zero, and by the exponentiation operator when the value of
the left operand is zero and the value of the exponent is negative, provided
that Real'Machine_Overflows is True; when Real'Machine_Overflows is False,
the result is unspecified.  {unspecified [partial]} [Constraint_Error can
also be raised when a finite result overflows (see G.2.6).]

        40.a   Discussion:  It is anticipated that an Ada binding to IEC
        559:1989 will be developed in the future.  As part of such a binding,
        the Machine_Overflows attribute of a conformant floating point type
        will be specified to yield False, which will permit implementations
        of the complex arithmetic operations to deliver results with an
        infinite component (and set the overflow flag defined by the binding)
        instead of raising Constraint_Error in overflow situations, when
        traps are disabled.  Similarly, it is appropriate for the complex
        arithmetic operations to deliver results with infinite components
        (and set the zero-divide flag defined by the binding) instead of
        raising Constraint_Error in the situations defined above, when traps
        are disabled.  Finally, such a binding should also specify the
        behavior of the complex arithmetic operations, when sensible, given
        operands with infinite components.


                         Implementation Requirements

41   In the implementation of Numerics.Generic_Complex_Types, the range of
intermediate values allowed during the calculation of a final result shall
not be affected by any range constraint of the subtype Real.

        41.a   Implementation Note:  Implementations of Numerics.Generic_
        Complex_Types written in Ada should therefore avoid declaring local
        variables of subtype Real; the subtype Real'Base should be used
        instead.

42   {prescribed result (for the evaluation of a complex arithmetic
operation)} In the following cases, evaluation of a complex arithmetic
operation shall yield the prescribed result, provided that the preceding
rules do not call for an exception to be raised:

   43  The results of the Re, Im, and Compose_From_Cartesian functions
       are exact.

   44  The real (resp., imaginary) component of the result of a binary
       addition operator that yields a result of complex type is exact
       when either of its operands is of pure-imaginary (resp., real)
       type.

 44.a   Ramification:  The result of the addition operator is exact when
        one of its operands is of real type and the other is of
        pure-imaginary type.  In this particular case, the operator is
        analogous to the Compose_From_Cartesian function; it performs no
        arithmetic.

   45  The real (resp., imaginary) component of the result of a binary
       subtraction operator that yields a result of complex type is
       exact when its right operand is of pure-imaginary (resp., real)
       type.

   46  The real component of the result of the Conjugate function for
       the complex type is exact.

   47  When the point in the complex plane represented by the parameter
       X lies on the nonnegative real axis, the Argument function yields
       a result of zero.

 47.a   Discussion:  Argument(X + i*Y) is analogous to EF.Arctan(Y, X),
        where EF is an appropriate instance of Numerics.Generic_
        Elementary_Functions, except when X and Y are both zero, in
        which case the former yields the value zero while the latter
        raises Numerics.Argument_Error.

   48  When the value of the parameter Modulus is zero, the Compose_
       From_Polar function yields a result of zero.

   49  When the value of the parameter Argument is equal to a multiple
       of the quarter cycle, the result of the Compose_From_Polar
       function with specified cycle lies on one of the axes.  In this
       case, one of its components is zero, and the other has the
       magnitude of the parameter Modulus.

   50  Exponentiation by a zero exponent yields the value one.
       Exponentiation by a unit exponent yields the value of the left
       operand.  Exponentiation of the value one yields the value one.
       Exponentiation of the value zero yields the value zero, provided
       that the exponent is nonzero.  When the left operand is of
       pure-imaginary type, one component of the result of the
       exponentiation operator is zero.

51   When the result, or a result component, of any operator of
Numerics.Generic_Complex_Types has a mathematical definition in terms of a
single arithmetic or relational operation, that result or result component
exhibits the accuracy of the corresponding operation of the type Real.

52   Other accuracy requirements for the Modulus, Argument, and Compose_From_
Polar functions, and accuracy requirements for the multiplication of a pair
of complex operands or for division by a complex operand, all of which apply
only in the strict mode, are given in G.2.6.

53   The sign of a zero result or zero result component yielded by a complex
arithmetic operation or function is implementation defined when Real'Signed_
Zeros is True.

        53.a   Implementation defined:  The sign of a zero result (or a
        component thereof) from any operator or function in Numerics.Generic_
        Complex_Types, when Real'Signed_Zeros is True.


                         Implementation Permissions

54   The nongeneric equivalent packages may, but need not, be actual
instantiations of the generic package for the appropriate predefined type.

55   Implementations may obtain the result of exponentiation of a complex or
pure-imaginary operand by repeated complex multiplication, with arbitrary
association of the factors and with a possible final complex reciprocation
(when the exponent is negative).  Implementations are also permitted to
obtain the result of exponentiation of a complex operand, but not of a
pure-imaginary operand, by converting the left operand to a polar
representation; exponentiating the modulus by the given exponent; multiplying
the argument by the given exponent, when the exponent is positive, or
dividing the argument by the absolute value of the given exponent, when the
exponent is negative; and reconverting to a cartesian representation.
Because of this implementation freedom, no accuracy requirement is imposed on
complex exponentiation (except for the prescribed results given above, which
apply regardless of the implementation method chosen).


                            Implementation Advice

56   Because the usual mathematical meaning of multiplication of a complex
operand and a real operand is that of the scaling of both components of the
former by the latter, an implementation should not perform this operation by
first promoting the real operand to complex type and then performing a full
complex multiplication.  In systems that, in the future, support an Ada
binding to IEC 559:1989, the latter technique will not generate the required
result when one of the components of the complex operand is infinite.
(Explicit multiplication of the infinite component by the zero component
obtained during promotion yields a NaN that propagates into the final
result.)  Analogous advice applies in the case of multiplication of a complex
operand and a pure-imaginary operand, and in the case of division of a
complex operand by a real or pure-imaginary operand.

57   Likewise, because the usual mathematical meaning of addition of a
complex operand and a real operand is that the imaginary operand remains
unchanged, an implementation should not perform this operation by first
promoting the real operand to complex type and then performing a full complex
addition.  In implementations in which the Signed_Zeros attribute of the
component type is True (and which therefore conform to IEC 559:1989 in regard
to the handling of the sign of zero in predefined arithmetic operations), the
latter technique will not generate the required result when the imaginary
component of the complex operand is a negatively signed zero.  (Explicit
addition of the negative zero to the zero obtained during promotion yields a
positive zero.)  Analogous advice applies in the case of addition of a
complex operand and a pure-imaginary operand, and in the case of subtraction
of a complex operand and a real or pure-imaginary operand.

58   Implementations in which Real'Signed_Zeros is True should attempt to
provide a rational treatment of the signs of zero results and result
components.  As one example, the result of the Argument function should have
the sign of the imaginary component of the parameter X when the point
represented by that parameter lies on the positive real axis; as another, the
sign of the imaginary component of the Compose_From_Polar function should be
the same as (resp., the opposite of) that of the Argument parameter when that
parameter has a value of zero and the Modulus parameter has a nonnegative
(resp., negative) value.


                         Wording Changes From Ada 83

        58.a   The semantics of Numerics.Generic_Complex_Types differs from
        Generic_Complex_Types as defined in ISO/IEC CD 13813 (for Ada 83) in
        the following ways:

         58.b  The generic package is a child of the package defining
               the Argument_Error exception.

         58.c  The nongeneric equivalents export types and constants
               with the same names as those exported by the generic
               package, rather than with names unique to the package.

         58.d  Implementations are not allowed to impose an optional
               restriction that the generic actual parameter associated
               with Real be unconstrained.  (In view of the ability to
               declare variables of subtype Real'Base in implementations
               of Numerics.Generic_Complex_Types, this flexibility is no
               longer needed.)

         58.e  The dependence of the Argument function on the sign of a
               zero parameter component is tied to the value of
               Real'Signed_Zeros.

         58.f  Conformance to accuracy requirements is conditional.



G.1.2 Complex Elementary Functions

                              Static Semantics

1   The generic library package Numerics.Generic_Complex_Elementary_Functions
has the following declaration:

2   with Ada.Numerics.Generic_Complex_Types;
    generic
       with package Complex_Types is new Ada.Numerics.Generic_Complex_Types (<>\
);
       use Complex_Types;
    package Ada.Numerics.Generic_Complex_Elementary_Functions is
       pragma Pure(Generic_Complex_Elementary_Functions);

3      function Sqrt (X : Complex)   return Complex;
       function Log  (X : Complex)   return Complex;
       function Exp  (X : Complex)   return Complex;
       function Exp  (X : Imaginary) return Complex;
       function "**" (Left : Complex;   Right : Complex)   return Complex;
       function "**" (Left : Complex;   Right : Real'Base) return Complex;
       function "**" (Left : Real'Base; Right : Complex)   return Complex;

4      function Sin (X : Complex) return Complex;
       function Cos (X : Complex) return Complex;
       function Tan (X : Complex) return Complex;
       function Cot (X : Complex) return Complex;

5      function Arcsin (X : Complex) return Complex;
       function Arccos (X : Complex) return Complex;
       function Arctan (X : Complex) return Complex;
       function Arccot (X : Complex) return Complex;

6      function Sinh (X : Complex) return Complex;
       function Cosh (X : Complex) return Complex;
       function Tanh (X : Complex) return Complex;
       function Coth (X : Complex) return Complex;

7      function Arcsinh (X : Complex) return Complex;
       function Arccosh (X : Complex) return Complex;
       function Arctanh (X : Complex) return Complex;
       function Arccoth (X : Complex) return Complex;

8   end Ada.Numerics.Generic_Complex_Elementary_Functions;

9   {Ada.Numerics.Complex_Elementary_Functions} The library package
Numerics.Complex_Elementary_Functions defines the same subprograms as
Numerics.Generic_Complex_Elementary_Functions, except that the predefined
type Float is systematically substituted for Real'Base, and the Complex and
Imaginary types exported by Numerics.Complex_Types are systematically
substituted for Complex and Imaginary, throughout.  Nongeneric equivalents of
Numerics.Generic_Complex_Elementary_Functions corresponding to each of the
other predefined floating point types are defined similarly, with the names
Numerics.Short_Complex_Elementary_Functions, Numerics.Long_Complex_
Elementary_Functions, etc.

        9.a   Reason:  The nongeneric equivalents are provided to allow the
        programmer to construct simple mathematical applications without
        being required to understand and use generics.

10   The overloading of the Exp function for the pure-imaginary type is
provided to give the user an alternate way to compose a complex value from a
given modulus and argument.  In addition to Compose_From_Polar(Rho, Theta)
(see G.1.1), the programmer may write Rho * Exp(i * Theta).

11   The imaginary (resp., real) component of the parameter X of the forward
hyperbolic (resp., trigonometric) functions and of the Exp function (and the
parameter X, itself, in the case of the overloading of the Exp function for
the pure-imaginary type) represents an angle measured in radians, as does the
imaginary (resp., real) component of the result of the Log and inverse
hyperbolic (resp., trigonometric) functions.

12   The functions have their usual mathematical meanings.  However, the
arbitrariness inherent in the placement of branch cuts, across which some of
the complex elementary functions exhibit discontinuities, is eliminated by
the following conventions:

   13  The imaginary component of the result of the Sqrt and Log
       functions is discontinuous as the parameter X crosses the
       negative real axis.

   14  The result of the exponentiation operator when the left operand
       is of complex type is discontinuous as that operand crosses the
       negative real axis.

   15  The real (resp., imaginary) component of the result of the Arcsin
       and Arccos (resp., Arctanh) functions is discontinuous as the
       parameter X crosses the real axis to the left of -1.0 or the
       right of 1.0.

   16  The real (resp., imaginary) component of the result of the Arctan
       (resp., Arcsinh) function is discontinuous as the parameter X
       crosses the imaginary axis below -i or above i.

   17  The real component of the result of the Arccot function is
       discontinuous as the parameter X crosses the imaginary axis
       between -i and i.

   18  The imaginary component of the Arccosh function is discontinuous
       as the parameter X crosses the real axis to the left of 1.0.

   19  The imaginary component of the result of the Arccoth function is
       discontinuous as the parameter X crosses the real axis between
       -1.0 and 1.0.

20   The computed results of the mathematically multivalued functions are
rendered single-valued by the following conventions, which are meant to imply
the principal branch:

   21  The real component of the result of the Sqrt and Arccosh
       functions is nonnegative.

   22  The same convention applies to the imaginary component of the
       result of the Log function as applies to the result of the
       natural-cycle version of the Argument function of Numerics.-
       Generic_Complex_Types (see G.1.1).

   23  The range of the real (resp., imaginary) component of the result
       of the Arcsin and Arctan (resp., Arcsinh and Arctanh) functions
       is approximately -Pi/2.0 to Pi/2.0.

   24  The real (resp., imaginary) component of the result of the Arccos
       and Arccot (resp., Arccoth) functions ranges from 0.0 to
       approximately Pi.

   25  The range of the imaginary component of the result of the Arccosh
       function is approximately -Pi to Pi.

26   In addition, the exponentiation operator inherits the single-valuedness
of the Log function.


                              Dynamic Semantics

27   The exception Numerics.Argument_Error is raised by the exponentiation
operator, signaling a parameter value outside the domain of the corresponding
mathematical function, when the value of the left operand is zero and the
real component of the exponent (or the exponent itself, when it is of real
type) is zero.

28   {Division_Check [partial]} {check, language-defined (Division_Check)}
{Constraint_Error (raised by failure of run-time check)} The exception
Constraint_Error is raised, signaling a pole of the mathematical function
(analogous to dividing by zero), in the following cases, provided that
Complex_Types.Real'Machine_Overflows is True:

   29  by the Log, Cot, and Coth functions, when the value of the
       parameter X is zero;

   30  by the exponentiation operator, when the value of the left
       operand is zero and the real component of the exponent (or the
       exponent itself, when it is of real type) is negative;

   31  by the Arctan and Arccot functions, when the value of the
       parameter X is +/-i;

   32  by the Arctanh and Arccoth functions, when the value of the
       parameter X is +/-1.0.

33   [Constraint_Error can also be raised when a finite result overflows (see
G.2.6); this may occur for parameter values sufficiently near poles, and, in
the case of some of the functions, for parameter values having components of
sufficiently large magnitude.]

        33.a   Reason:  The purpose of raising Constraint_Error (rather than
        Numerics.Argument_Error) at the poles of a function, when Float_
        Type'Machine_Overflows is True, is to provide continuous behavior as
        the actual parameters of the function approach the pole and finally
        reach it.

{unspecified [partial]} When Complex_Types.Real'Machine_Overflows is False,
the result at poles is unspecified.

        33.b   Discussion:  It is anticipated that an Ada binding to IEC
        559:1989 will be developed in the future.  As part of such a binding,
        the Machine_Overflows attribute of a conformant floating point type
        will be specified to yield False, which will permit implementations
        of the complex elementary functions to deliver results with an
        infinite component (and set the overflow flag defined by the binding)
        instead of raising Constraint_Error in overflow situations, when
        traps are disabled.  Similarly, it is appropriate for the complex
        elementary functions to deliver results with an infinite component
        (and set the zero-divide flag defined by the binding) instead of
        raising Constraint_Error at poles, when traps are disabled.  Finally,
        such a binding should also specify the behavior of the complex
        elementary functions, when sensible, given parameters with infinite
        components.


                         Implementation Requirements

34   In the implementation of Numerics.Generic_Complex_Elementary_Functions,
the range of intermediate values allowed during the calculation of a final
result shall not be affected by any range constraint of the subtype Complex_
Types.Real.

        34.a   Implementation Note:  Implementations of Numerics.Generic_
        Complex_Elementary_Functions written in Ada should therefore avoid
        declaring local variables of subtype Complex_Types.Real; the subtype
        Complex_Types.Real'Base should be used instead.

35   {prescribed result (for the evaluation of a complex elementary
function)} In the following cases, evaluation of a complex elementary
function shall yield the prescribed result (or a result having the prescribed
component), provided that the preceding rules do not call for an exception to
be raised:

   36  When the parameter X has the value zero, the Sqrt, Sin, Arcsin,
       Tan, Arctan, Sinh, Arcsinh, Tanh, and Arctanh functions yield a
       result of zero; the Exp, Cos, and Cosh functions yield a result
       of one; the Arccos and Arccot functions yield a real result; and
       the Arccoth function yields an imaginary result.

   37  When the parameter X has the value one, the Sqrt function yields
       a result of one; the Log, Arccos, and Arccosh functions yield a
       result of zero; and the Arcsin function yields a real result.

   38  When the parameter X has the value -1.0, the Sqrt function yields
       the result

          39  i (resp., -i), when the sign of the imaginary component of
              X is positive (resp., negative), if Complex_Types.-
              Real'Signed_Zeros is True;

          40  i, if Complex_Types.Real'Signed_Zeros is False;

   41  the Log function yields an imaginary result; and the Arcsin and
       Arccos functions yield a real result.

   42  When the parameter X has the value +/-i, the Log function yields
       an imaginary result.

   43  Exponentiation by a zero exponent yields the value one.
       Exponentiation by a unit exponent yields the value of the left
       operand (as a complex value).  Exponentiation of the value one
       yields the value one.  Exponentiation of the value zero yields
       the value zero.

        43.a   Discussion:  It is possible to give many other prescribed
        results restricting the result to the real or imaginary axis when the
        parameter X is appropriately restricted to easily testable portions
        of the domain.  We follow the proposed ISO/IEC standard for Generic_
        Complex_Elementary_Functions (for Ada 83), CD 13813, in not doing so,
        however.

44   Other accuracy requirements for the complex elementary functions, which
apply only in the strict mode, are given in G.2.6.

45   The sign of a zero result or zero result component yielded by a complex
elementary function is implementation defined when Complex_Types.Real'Signed_
Zeros is True.

        45.a   Implementation defined:  The sign of a zero result (or a
        component thereof) from any operator or function in Numerics.Generic_
        Complex_Elementary_Functions, when Complex_Types.Real'Signed_Zeros is
        True.


                         Implementation Permissions

46   The nongeneric equivalent packages may, but need not, be actual
instantiations of the generic package with the appropriate predefined
nongeneric equivalent of Numerics.Generic_Complex_Types; if they are, then
the latter shall have been obtained by actual instantiation of
Numerics.Generic_Complex_Types.

47   The exponentiation operator may be implemented in terms of the Exp and
Log functions.  Because this implementation yields poor accuracy in some
parts of the domain, no accuracy requirement is imposed on complex
exponentiation.

48   {unspecified [partial]} The implementation of the Exp function of a
complex parameter X is allowed to raise the exception Constraint_Error,
signaling overflow, when the real component of X exceeds an unspecified
threshold that is approximately log (Complex_Types.Real'Safe_Last).  This
permission recognizes the impracticality of avoiding overflow in the marginal
case that the exponential of the real component of X exceeds the safe range
of Complex_Types.Real but both components of the final result do not.
Similarly, the Sin and Cos (resp., Sinh and Cosh) functions are allowed to
raise the exception Constraint_Error, signaling overflow, when the absolute
value of the imaginary (resp., real) component of the parameter X exceeds an
unspecified threshold that is approximately log (Complex_Types.Real'Safe_
Last)+log (2.0).  {unspecified [partial]} This permission recognizes the
impracticality of avoiding overflow in the marginal case that the hyperbolic
sine or cosine of the imaginary (resp., real) component of X exceeds the safe
range of Complex_Types.Real but both components of the final result do not.
                            Implementation Advice

49   Implementations in which Complex_Types.Real'Signed_Zeros is True should
attempt to provide a rational treatment of the signs of zero results and
result components.  For example, many of the complex elementary functions
have components that are odd functions of one of the parameter components; in
these cases, the result component should have the sign of the parameter
component at the origin.  Other complex elementary functions have zero
components whose sign is opposite that of a parameter component at the
origin, or is always positive or always negative.


                         Wording Changes From Ada 83

        49.a   The semantics of Numerics.Generic_Complex_Elementary_Functions
        differs from Generic_Complex_Elementary_Functions as defined in
        ISO/IEC CD 13814 (for Ada 83) in the following ways:

         49.b  The generic package is a child unit of the package
               defining the Argument_Error exception.

         49.c  The proposed Generic_Complex_Elementary_Functions stan-
               dard (for Ada 83) specified names for the nongeneric
               equivalents, if provided.  Here, those nongeneric
               equivalents are required.

         49.d  The generic package imports an instance of Numerics.-
               Generic_Complex_Types rather than a long list of
               individual types and operations exported by such an
               instance.

         49.e  The dependence of the imaginary component of the Sqrt and
               Log functions on the sign of a zero parameter component
               is tied to the value of Complex_Types.Real'Signed_Zeros.

         49.f  Conformance to accuracy requirements is conditional.



G.1.3 Complex Input-Output

1   The generic package Text_IO.Complex_IO defines procedures for the
formatted input and output of complex values.  The generic actual parameter
in an instantiation of Text_IO.Complex_IO is an instance of Numerics.Generic_
Complex_Types for some floating point subtype.  Exceptional conditions are
reported by raising the appropriate exception defined in Text_IO.

        1.a   Implementation Note:  An implementation of Text_IO.Complex_IO
        can be built around an instance of Text_IO.Float_IO for the base
        subtype of Complex_Types.Real, where Complex_Types is the generic
        formal package parameter of Text_IO.Complex_IO.  There is no need for
        an implementation of Text_IO.Complex_IO to parse real values.


                              Static Semantics

2   The generic library package Text_IO.Complex_IO has the following
declaration:

        2.a   Ramification:  Because this is a child of Text_IO, the
        declarations of the visible part of Text_IO are directly visible
        within it.

3   with Ada.Numerics.Generic_Complex_Types;
    generic
       with package Complex_Types is new Ada.Numerics.Generic_Complex_Types (<>\
);
    package Ada.Text_IO.Complex_IO is

4      use Complex_Types;

5      Default_Fore : Field := 2;
       Default_Aft  : Field := Real'Digits - 1;
       Default_Exp  : Field := 3;

6      procedure Get (File  : in  File_Type;
                      Item  : out Complex;
                      Width : in  Field := 0);
       procedure Get (Item  : out Complex;
                      Width : in  Field := 0);

7      procedure Put (File : in File_Type;
                      Item : in Complex;
                      Fore : in Field := Default_Fore;
                      Aft  : in Field := Default_Aft;
                      Exp  : in Field := Default_Exp);
       procedure Put (Item : in Complex;
                      Fore : in Field := Default_Fore;
                      Aft  : in Field := Default_Aft;
                      Exp  : in Field := Default_Exp);

8      procedure Get (From : in  String;
                      Item : out Complex;
                      Last : out Positive);
       procedure Put (To   : out String;
                      Item : in  Complex;
                      Aft  : in  Field := Default_Aft;
                      Exp  : in  Field := Default_Exp);

9   end Ada.Text_IO.Complex_IO;

10   The semantics of the Get and Put procedures are as follows:


11  procedure Get (File  : in  File_Type;
                   Item  : out Complex;
                   Width : in  Field := 0);
    procedure Get (Item  : out Complex;
                   Width : in  Field := 0);

        12   The input sequence is a pair of optionally signed real literals
        representing the real and imaginary components of a complex value;
        optionally, the pair of components may be separated by a comma and/or
        surrounded by a pair of parentheses.  Blanks are freely allowed
        before each of the components and before the parentheses and comma,
        if either is used.  If the value of the parameter Width is zero, then

           13  line and page terminators are also allowed in these
               places;

           14  the components shall be separated by at least one blank
               or line terminator if the comma is omitted; and

           15  reading stops when the right parenthesis has been read,
               if the input sequence includes a left parenthesis, or
               when the imaginary component has been read, otherwise.

        If a nonzero value of Width is supplied, then

           16  the components shall be separated by at least one blank
               if the comma is omitted; and

           17  exactly Width characters are read, or the characters
               (possibly none) up to a line terminator, whichever comes
               first (blanks are included in the count).

        17.a   Reason:  The parenthesized and comma-separated form is the
        form produced by Put on output (see below), and also by list-directed
        output in Fortran.  The other allowed forms match several common
        styles of edit-directed output in Fortran, allowing most preexisting
        Fortran data files containing complex data to be read easily.  When
        such files contain complex values with no separation between the real
        and imaginary components, the user will have to read those components
        separately, using an instance of Text_IO.Float_IO.

        18   Returns, in the parameter Item, the value of type Complex that
        corresponds to the input sequence.
        19   The exception Text_IO.Data_Error is raised if the input sequence
        does not have the required syntax or if the components of the complex
        value obtained are not of the base subtype of Complex_Types.Real.


20  procedure Put (File : in File_Type;
                   Item : in Complex;
                   Fore : in Field := Default_Fore;
                   Aft  : in Field := Default_Aft;
                   Exp  : in Field := Default_Exp);
    procedure Put (Item : in Complex;
                   Fore : in Field := Default_Fore;
                   Aft  : in Field := Default_Aft;
                   Exp  : in Field := Default_Exp);

        21   Outputs the value of the parameter Item as a pair of decimal
        literals representing the real and imaginary components of the
        complex value, using the syntax of an aggregate.  More specifically,

           22  outputs a left parenthesis;

           23  outputs the value of the real component of the parameter
               Item with the format defined by the corresponding Put
               procedure of an instance of Text_IO.Float_IO for the base
               subtype of Complex_Types.Real, using the given values of
               Fore, Aft, and Exp;

           24  outputs a comma;

           25  outputs the value of the imaginary component of the
               parameter Item with the format defined by the
               corresponding Put procedure of an instance of
               Text_IO.Float_IO for the base subtype of Complex_
               Types.Real, using the given values of Fore, Aft, and Exp;

           26  outputs a right parenthesis.

        26.a   Discussion:  If the file has a bounded line length, a line
        terminator may be output implicitly before any element of the
        sequence itemized above.

        26.b   Discussion:  The option of outputting the complex value as a
        pair of reals without additional punctuation is not provided, since
        it can be accomplished by outputting the real and imaginary
        components of the complex value separately.


27  procedure Get (From : in  String;
                   Item : out Complex;
                   Last : out Positive);

        28   Reads a complex value from the beginning of the given string,
        following the same rule as the Get procedure that reads a complex
        value from a file, but treating the end of the string as a line
        terminator.  Returns, in the parameter Item, the value of type
        Complex that corresponds to the input sequence.  Returns in Last the
        index value such that From(Last) is the last character read.
        29   The exception Text_IO.Data_Error is raised if the input sequence
        does not have the required syntax or if the components of the complex
        value obtained are not of the base subtype of Complex_Types.Real.


30  procedure Put (To   : out String;
                   Item : in  Complex;
                   Aft  : in  Field := Default_Aft;
                   Exp  : in  Field := Default_Exp);

        31   Outputs the value of the parameter Item to the given string as a
        pair of decimal literals representing the real and imaginary
        components of the complex value, using the syntax of an aggregate.
        More specifically,

           32  a left parenthesis, the real component, and a comma are
               left justified in the given string, with the real
               component having the format defined by the Put procedure
               (for output to a file) of an instance of Text_IO.Float_IO
               for the base subtype of Complex_Types.Real, using a value
               of zero for Fore and the given values of Aft and Exp;

           33  the imaginary component and a right parenthesis are right
               justified in the given string, with the imaginary
               component having the format defined by the Put procedure
               (for output to a file) of an instance of Text_IO.Float_IO
               for the base subtype of Complex_Types.Real, using a value
               for Fore that completely fills the remainder of the
               string, together with the given values of Aft and Exp.

        33.a   Reason:  This rule is the one proposed in LSN-1051.  Other
        rules were considered, including one that would have read ``Outputs
        the value of the parameter Item to the given string, following the
        same rule as for output to a file, using a value for Fore such that
        the sequence of characters output exactly fills, or comes closest to
        filling, the string; in the latter case, the string is filled by
        inserting one extra blank immediately after the comma.''  While this
        latter rule might be considered the closest analogue to the rule for
        output to a string in Text_IO.Float_IO, it requires a more difficult
        and inefficient implementation involving special cases when the
        integer part of one component is substantially longer than that of
        the other and the string is too short to allow both to be preceded by
        blanks.  Unless such a special case applies, the latter rule might
        produce better columnar output if several such strings are ultimately
        output to a file, but very nearly the same output can be produced by
        outputting to the file directly, with the appropriate value of Fore;
        in any case, it might validly be assumed that output to a string is
        intended for further computation rather than for display, so that the
        precise formatting of the string to achieve a particular appearance
        is not the major concern.

        34   The exception Text_IO.Layout_Error is raised if the given string
        is too short to hold the formatted output.


                         Implementation Permissions

35   Other exceptions declared (by renaming) in Text_IO may be raised by the
preceding procedures in the appropriate circumstances, as for the
corresponding procedures of Text_IO.Float_IO.



G.1.4 The Package Wide_Text_IO.Complex_IO

                              Static Semantics

1   {Ada.Wide_Text_IO.Complex_IO} Implementations shall also provide the
generic library package Wide_Text_IO.Complex_IO.  Its declaration is obtained
from that of Text_IO.Complex_IO by systematically replacing Text_IO by Wide_
Text_IO and String by Wide_String; the description of its behavior is
obtained by additionally replacing references to particular characters
(commas, parentheses, etc.) by those for the corresponding wide characters.


{94-4574.c} {94-4889.i}



G.2 Numeric Performance Requirements

                         Implementation Requirements

1   {accuracy} {strict mode} Implementations shall provide a user-selectable
mode in which the accuracy and other numeric performance requirements
detailed in the following subclauses are observed.  This mode, referred to as
the strict mode, may or may not be the default mode; it directly affects the
results of the predefined arithmetic operations of real types and the results
of the subprograms in children of the Numerics package, and indirectly
affects the operations in other language defined packages.  {94-4983.c}
{relaxed mode} Implementations shall also provide the opposing mode, which is
known as the relaxed mode.

        1.a   Reason:  On the assumption that the users of an implementation
        that does not support the Numerics Annex have no particular need for
        numerical performance, such an implementation has no obligation to
        meet any particular requirements in this area.  On the other hand,
        users of an implementation that does support the Numerics Annex are
        provided with a way of ensuring that their programs achieve a known
        level of numerical performance and that the performance is portable
        to other such implementations.  The relaxed mode is provided to allow
        implementers to offer an efficient but not fully accurate alternative
        in the case that the strict mode entails a time overhead that some
        users may find excessive.  In some of its areas of impact, the
        relaxed mode may be fully equivalent to the strict mode.

        1.b   Implementation Note:  The relaxed mode may, for example, be
        used to exploit the implementation of (some of) the elementary
        functions in hardware, when available.  Such implementations often do
        not meet the accuracy requirements of the strict mode, or do not meet
        them over the specified range of parameter values, but compensate in
        other ways that may be important to the user, such as their extreme
        speed.

        1.c   Ramification:  For implementations supporting the Numerics
        Annex, the choice of mode has no effect on the selection of a
        representation for a real type or on the values of attributes of a
        real type.


                         Implementation Permissions

2   Either mode may be the default mode.

        2.a   Implementation defined:  Whether the strict mode or the relaxed
        mode is the default.

3   The two modes need not actually be different.


                            Extensions to Ada 83

        3.a   {extensions to Ada 83} The choice between strict and relaxed
        numeric performance was not available in Ada 83.



G.2.1 Model of Floating Point Arithmetic

1   In the strict mode, the predefined operations of a floating point type
shall satisfy the accuracy requirements specified here and shall avoid or
signal overflow in the situations described.  This behavior is presented in
terms of a model of floating point arithmetic that builds on the concept of
the canonical form (see A.5.3).


                              Static Semantics

2   Associated with each floating point type is an infinite set of model
numbers.  The model numbers of a type are used to define the accuracy
requirements that have to be satisfied by certain predefined operations of
the type; through certain attributes of the model numbers, they are also used
to explain the meaning of a user-declared floating point type declaration.
The model numbers of a derived type are those of the parent type; the model
numbers of a subtype are those of its type.

3   {model number} The model numbers of a floating point type T are zero and
all the values expressible in the canonical form (for the type T), in which
mantissa has T'Model_Mantissa digits and exponent has a value greater than or
equal to T'Model_Emin.  (These attributes are defined in G.2.2.)

        3.a   Discussion:  The model is capable of describing the behavior of
        most existing hardware that has a mantissa-exponent representation.
        As applied to a type T, it is parameterized by the values of
        T'Machine_Radix, T'Model_Mantissa, T'Model_Emin, T'Safe_First, and
        T'Safe_Last.  The values of these attributes are determined by how,
        and how well, the hardware behaves.  They in turn determine the set
        of model numbers and the safe range of the type, which figure in the
        accuracy and range (overflow avoidance) requirements.

        3.b   In hardware that is free of arithmetic anomalies, T'Model_
        Mantissa, T'Model_Emin, T'Safe_First, and T'Safe_Last will yield the
        same values as T'Machine_Mantissa, T'Machine_Emin, T'Base'First, and
        T'Base'Last, respectively, and the model numbers in the safe range of
        the type T will coincide with the machine numbers of the type T. In
        less perfect hardware, it is not possible for the model-oriented
        attributes to have these optimal values, since the hardware, by
        definition, and therefore the implementation, cannot conform to the
        stringencies of the resulting model; in this case, the values yielded
        by the model-oriented parameters have to be made more conservative
        (i.e., have to be penalized), with the result that the model numbers
        are more widely separated than the machine numbers, and the safe
        range is a subrange of the base range.  The implementation will then
        be able to conform to the requirements of the weaker model defined by
        the sparser set of model numbers and the smaller safe range.

4   {model interval} A model interval of a floating point type is any
interval whose bounds are model numbers of the type.  {model interval
(associated with a value)} The model interval of a type T associated with a
value v is the smallest model interval of T that includes v.  (The model
interval associated with a model number of a type consists of that number
only.)


                         Implementation Requirements
5   The accuracy requirements for the evaluation of certain predefined
operations of floating point types are as follows.

        5.a   Discussion:  This subclause does not cover the accuracy of an
        operation of a static expression; such operations have to be
        evaluated exactly (see 4.9).  It also does not cover the accuracy of
        the predefined attributes of a floating point subtype that yield a
        value of the type; such operations also yield exact results (see
        3.5.8 and A.5.3).

6   {operand interval} An operand interval is the model interval, of the type
specified for the operand of an operation, associated with the value of the
operand.

7   For any predefined arithmetic operation that yields a result of a
floating point type T, the required bounds on the result are given by a model
interval of T (called the result interval) defined in terms of the operand
values as follows:

    8  {result interval (for the evaluation of a predefined arithmetic
       operation)} The result interval is the smallest model interval of
       T that includes the minimum and the maximum of all the values
       obtained by applying the (exact) mathematical operation to values
       arbitrarily selected from the respective operand intervals.

9   The result interval of an exponentiation is obtained by applying the
above rule to the sequence of multiplications defined by the exponent,
assuming arbitrary association of the factors, and to the final division in
the case of a negative exponent.

10   The result interval of a conversion of a numeric value to a floating
point type T is the model interval of T associated with the operand value,
except when the source expression is of a fixed point type with a small that
is not a power of T'Machine_Radix or is a fixed point multiplication or
division either of whose operands has a small that is not a power of
T'Machine_Radix; in these cases, the result interval is implementation
defined.

        10.a   Implementation defined:  The result interval in certain cases
        of fixed-to-float conversion.

11   {Overflow_Check [partial]} {check, language-defined (Overflow_Check)}
For any of the foregoing operations, the implementation shall deliver a value
that belongs to the result interval when both bounds of the result interval
are in the safe range of the result type T, as determined by the values of
T'Safe_First and T'Safe_Last; otherwise,

   12  {Constraint_Error (raised by failure of run-time check)} if
       T'Machine_Overflows is True, the implementation shall either
       deliver a value that belongs to the result interval or raise
       Constraint_Error;

   13  if T'Machine_Overflows is False, the result is implementation
       defined.

 13.a   Implementation defined:  The result of a floating point
        arithmetic operation in overflow situations, when the Machine_
        Overflows attribute of the result type is False.

14   For any predefined relation on operands of a floating point type T, the
implementation may deliver any value (i.e., either True or False) obtained by
applying the (exact) mathematical comparison to values arbitrarily chosen
from the respective operand intervals.

15   The result of a membership test is defined in terms of comparisons of
the operand value with the lower and upper bounds of the given range or type
mark (the usual rules apply to these comparisons).


                         Implementation Permissions

16   If the underlying floating point hardware implements division as
multiplication by a reciprocal, the result interval for division (and
exponentiation by a negative exponent) is implementation defined.

        16.a   Implementation defined:  The result interval for division (or
        exponentiation by a negative exponent), when the floating point
        hardware implements division as multiplication by a reciprocal.


                         Wording Changes From Ada 83

        16.b   The Ada 9X model numbers of a floating point type that are in
        the safe range of the type are comparable to the Ada 83 safe numbers
        of the type.  There is no analog of the Ada 83 model numbers.  The
        Ada 9X model numbers, when not restricted to the safe range, are an
        infinite set.

                         Inconsistencies With Ada 83

        16.c   {inconsistencies with Ada 83} Giving the model numbers the
        hardware radix, instead of always a radix of two, allows (in
        conjunction with other changes) some borderline declared types to be
        represented with less precision than in Ada 83 (i.e., with single
        precision, whereas Ada 83 would have used double precision).  Because
        the lower precision satisfies the requirements of the model (and did
        so in Ada 83 as well), this change is viewed as a desirable
        correction of an anomaly, rather than a worrisome inconsistency.  (Of
        course, the wider representation chosen in Ada 83 also remains
        eligible for selection in Ada 9X.)

        16.d   As an example of this phenomenon, assume that Float is
        represented in single precision and that a double precision type is
        also available.  Also assume hexadecimal hardware with clean
        properties, for example certain IBM hardware.  Then,

16.e        type T is digits Float'Digits range -Float'Last .. Float'Last;

        16.f   results in T being represented in double precision in Ada 83
        and in single precision in Ada 9X.  The latter is intuitively
        correct; the former is counterintuitive.  The reason why the double
        precision type is used in Ada 83 is that Float has model and safe
        numbers (in Ada 83) with 21 binary digits in their mantissas, as is
        required to model the hypothesized hexadecimal hardware using a
        binary radix; thus Float'Last, which is not a model number, is
        slightly outside the range of safe numbers of the single precision
        type, making that type ineligible for selection as the representation
        of T even though it provides adequate precision.  In Ada 9X,
        Float'Last (the same value as before) is a model number and is in the
        safe range of Float on the hypothesized hardware, making Float
        eligible for the representation of T.

                            Extensions to Ada 83

        16.g   {extensions to Ada 83} Giving the model numbers the hardware
        radix allows for practical implementations on decimal hardware.

                         Wording Changes From Ada 83

        16.h   The wording of the model of floating point arithmetic has been
        simplified to a large extent.



G.2.2 Model-Oriented Attributes of Floating Point Types

1   In implementations that support the Numerics Annex, the model-oriented
attributes of floating point types shall yield the values defined here, in
both the strict and the relaxed modes.  These definitions add conditions to
those in A.5.3.


                              Static Semantics

2   For every subtype S of a floating point type T:

3   S'Model_Mantissa
                Yields the number of digits in the mantissa of the canonical
                form of the model numbers of T (see A.5.3).  The value of
                this attribute shall be greater than or equal to
                Ceiling(d*log (10)/log (T'Machine_Radix))+1, where d is the
                requested decimal precision of T.  In addition, it shall be
                less than or equal to the value of T'Machine_Mantissa.  This
                attribute yields a value of the type universal_integer.

3.a     Ramification:  S'Model_Epsilon, which is defined in terms of S'Model_
        Mantissa (see A.5.3), yields the absolute value of the difference
        between one and the next model number of the type T above one.  It is
        equal to or larger than the absolute value of the difference between
        one and the next machine number of the type T above one.

4   S'Model_Emin
                Yields the minimum exponent of the canonical form of the
                model numbers of T (see A.5.3).  The value of this attribute
                shall be greater than or equal to the value of T'Machine_
                Emin.  This attribute yields a value of the type universal_
                integer.

4.a     Ramification:  S'Model_Small, which is defined in terms of S'Model_
        Emin (see A.5.3), yields the smallest positive (nonzero) model number
        of the type T.

5   S'Safe_First
                Yields the lower bound of the safe range of T.  The value of
                this attribute shall be a model number of T and greater than
                or equal to the lower bound of the base range of T.  In
                addition, if T is declared by a floating_point_definition or
                is derived from such a type, and the floating_point_
                definition includes a real_range_specification specifying a
                lower bound of lb, then the value of this attribute shall be
                less than or equal to lb; otherwise, it shall be less than or
                              4*d
                equal to -10.0   , where d is the requested decimal precision
                of T.  This attribute yields a value of the type universal_
                real.

6   S'Safe_Last
                Yields the upper bound of the safe range of T.  The value of
                this attribute shall be a model number of T and less than or
                equal to the upper bound of the base range of T.  In
                addition, if T is declared by a floating_point_definition or
                is derived from such a type, and the floating_point_
                definition includes a real_range_specification specifying an
                upper bound of ub, then the value of this attribute shall be
                greater than or equal to ub; otherwise, it shall be greater
                                     4*d
                than or equal to 10.0   , where d is the requested decimal
                precision of T.  This attribute yields a value of the type
                universal_real.

7   {Constraint_Error (raised by failure of run-time check)}
                S'Model
                Denotes a function (of a parameter X) whose specification is
                given in A.5.3.  If X is a model number of T, the function
                yields X; otherwise, it yields the value obtained by rounding
                or truncating X to either one of the adjacent model numbers
                of T.  {Overflow_Check [partial]} {check, language-defined
                (Overflow_Check)} Constraint_Error is raised if the resulting
                model number is outside the safe range of S. A zero result
                has the sign of X when S'Signed_Zeros is True.

8   Subject to the constraints given above, the values of S'Model_Mantissa
and S'Safe_Last are to be maximized, and the values of S'Model_Emin and
S'Safe_First minimized, by the implementation as follows:

    9  First, S'Model_Mantissa is set to the largest value for which
       values of S'Model_Emin, S'Safe_First, and S'Safe_Last can be
       chosen so that the implementation satisfies the strict-mode
       requirements of G.2.1 in terms of the model numbers and safe
       range induced by these attributes.

   10  Next, S'Model_Emin is set to the smallest value for which values
       of S'Safe_First and S'Safe_Last can be chosen so that the
       implementation satisfies the strict-mode requirements of G.2.1 in
       terms of the model numbers and safe range induced by these
       attributes and the previously determined value of S'Model_
       Mantissa.

   11  Finally, S'Safe_First and S'Safe_last are set (in either order)
       to the smallest and largest values, respectively, for which the
       implementation satisfies the strict-mode requirements of G.2.1 in
       terms of the model numbers and safe range induced by these
       attributes and the previously determined values of S'Model_
       Mantissa and S'Model_Emin.

{94-4934.a} {94-4878.a} {94-4455.a} {94-4889.a}

        11.a   Ramification:  {IEEE floating point arithmetic} {IEC 559:1989}
        The following table shows appropriate attribute values for IEEE basic
        single and double precision types (ANSI/IEEE Std 754-1985, IEC
        559:1989).  Here, we use the names IEEE_Float_32 and IEEE_Float_64,
        the names that would typically be declared in package Interfaces, in
        an implementation that supports IEEE arithmetic.  In such an
        implementation, the attributes would typically be the same for
        Standard.Float and Long_Float, respectively.

11.b        Attribute                        IEEE_Float_32                 IEEE\
_Float_64

11.c        'Machine_Radix                               2                     \
        2
            'Machine_Mantissa                           24                     \
       53
            'Machine_Emin                             -125                     \
    -1021
            'Machine_Emax                              128                     \
     1024
            'Denorm                                   True                     \
     True
            'Machine_Rounds                           True                     \
     True
            'Machine_Overflows                  True/False                    T\
rue/False
            'Signed_Zeros                   should be True                shoul\
d be True

11.d        'Model_Mantissa    (same as 'Machine_Mantissa)   (same as 'Machine_\
Mantissa)
            'Model_Emin            (same as 'Machine_Emin)       (same as 'Mach\
ine_Emin)
            'Model_Epsilon                      2.0**(-23)                    2\
.0**(-52)
            'Model_Small                       2.0**(-126)                  2.0\
**(-1022)
            'Safe_First         -2.0**128*(1.0-2.0**(-24))   -2.0**1024*(1.0-2.\
0**(-53))
            'Safe_Last           2.0**128*(1.0-2.0**(-24))    2.0**1024*(1.0-2.\
0**(-53))

11.e        'Digits                                      6                     \
       15
            'Base'Digits                 (same as 'Digits)             (same as\
 'Digits)

11.f        'First                   (same as 'Safe_First)         (same as 'Sa\
fe_First)
            'Last                     (same as 'Safe_Last)          (same as 'S\
afe_Last)
            'Size                                       32                     \
       64

        11.g   Note: 'Machine_Overflows can be True or False, depending on
        whether the Ada implementation raises Constraint_Error or delivers a
        signed infinity in overflow and zerodivide situations (and at poles
        of the elementary functions).  {94-4893.c} {94-4900.a}



G.2.3 Model of Fixed Point Arithmetic

1   In the strict mode, the predefined arithmetic operations of a fixed point
type shall satisfy the accuracy requirements specified here and shall avoid
or signal overflow in the situations described.


                         Implementation Requirements

2   The accuracy requirements for the predefined fixed point arithmetic
operations and conversions, and the results of relations on fixed point
operands, are given below.

        2.a   Discussion:  This subclause does not cover the accuracy of an
        operation of a static expression; such operations have to be
        evaluated exactly (see 4.9).

3   The operands of the fixed point adding operators, absolute value, and
comparisons have the same type.  These operations are required to yield exact
results, unless they overflow.

4   Multiplications and divisions are allowed between operands of any two
fixed point types; the result has to be (implicitly or explicitly) converted
to some other numeric type.  For purposes of defining the accuracy rules, the
multiplication or division and the conversion are treated as a single
operation whose accuracy depends on three types (those of the operands and
the result).  For decimal fixed point types, the attribute T'Round may be
used to imply explicit conversion with rounding (see 3.5.10).

5   When the result type is a floating point type, the accuracy is as given
in G.2.1.  {perfect result set} For some combinations of the operand and
result types in the remaining cases, the result is required to belong to a
small set of values called the perfect result set; {close result set} for
other combinations, it is required merely to belong to a generally larger and
implementation-defined set of values called the close result set.  When the
result type is a decimal fixed point type, the perfect result set contains a
single value; thus, operations on decimal types are always fully specified.

        5.a   Implementation defined:  The definition of close result set,
        which determines the accuracy of certain fixed point multiplications
        and divisions.

6   When one operand of a fixed-fixed multiplication or division is of type
universal_real, that operand is not implicitly converted in the usual sense,
since the context does not determine a unique target type, but the accuracy
of the result of the multiplication or division (i.e., whether the result has
to belong to the perfect result set or merely the close result set) depends
on the value of the operand of type universal_real and on the types of the
other operand and of the result.

        6.a   Discussion:  We need not consider here the multiplication or
        division of two such operands, since in that case either the
        operation is evaluated exactly (i.e., it is an operation of a static
        expression all of whose operators are of a root numeric type) or it
        is considered to be an operation of a floating point type.

7   For a fixed point multiplication or division whose (exact) mathematical
result is v, and for the conversion of a value v to a fixed point type, the
perfect result set and close result set are defined as follows:

    8   If the result type is an ordinary fixed point type with a small
       of s,

           9  if v is an integer multiple of s, then the perfect result
              set contains only the value v;

          10  otherwise, it contains the integer multiple of s just
              below v and the integer multiple of s just above v.

       11   The close result set is an implementation-defined set of
       consecutive integer multiples of s containing the perfect result
       set as a subset.

   12   If the result type is a decimal type with a small of s,

          13  if v is an integer multiple of s, then the perfect result
              set contains only the value v;

          14  otherwise, if truncation applies then it contains only the
              integer multiple of s in the direction toward zero,
              whereas if rounding applies then it contains only the
              nearest integer multiple of s (with ties broken by
              rounding away from zero).

       15   The close result set is an implementation-defined set of
       consecutive integer multiples of s containing the perfect result
       set as a subset.

        15.a   Ramification:  As a consequence of subsequent rules, this
        case does not arise when the operand types are also decimal
        types.

   16   If the result type is an integer type,

          17  if v is an integer, then the perfect result set contains
              only the value v;

          18  otherwise, it contains the integer nearest to the value v
              (if v lies equally distant from two consecutive integers,
              the perfect result set contains the one that is further
              from zero).  {94-4920.a}

       19   The close result set is an implementation-defined set of
       consecutive integers containing the perfect result set as a
       subset.

20   The result of a fixed point multiplication or division shall belong
either to the perfect result set or to the close result set, as described
below, if overflow does not occur.  In the following cases, if the result
type is a fixed point type, let s be its small; otherwise, i.e. when the
result type is an integer type, let s be 1.0.

   21  For a multiplication or division neither of whose operands is of
       type universal_real, let l and r be the smalls of the left and
       right operands.  For a multiplication, if (l*r)/s is an integer
       or the reciprocal of an integer (the smalls are said to be
       ``compatible'' in this case), the result shall belong to the
       perfect result set; otherwise, it belongs to the close result
       set.  For a division, if l/(r*s) is an integer or the reciprocal
       of an integer (i.e., the smalls are compatible), the result shall
       belong to the perfect result set; otherwise, it belongs to the
       close result set.

 21.a   Ramification:  When the operand and result types are all decimal
        types, their smalls are necessarily compatible; the same is true
        when they are all ordinary fixed point types with binary smalls.

   22  For a multiplication or division having one universal_real
       operand with a value of v, note that it is always possible to
       factor v as an integer multiple of a ``compatible'' small, but
       the integer multiple may be ``too big.''  If there exists a
       factorization in which that multiple is less than some
       implementation-defined limit, the result shall belong to the
       perfect result set; otherwise, it belongs to the close result
       set.  {94-4952.a}

 22.a   Implementation defined:  Conditions on a universal_real operand
        of a fixed point multiplication or division for which the result
        shall be in the perfect result set.

23   A multiplication P * Q of an operand of a fixed point type F by an
operand of an integer type I, or vice-versa, and a division P / Q of an
operand of a fixed point type F by an operand of an integer type I, are also
allowed.  {94-4768.r} {94-4889.l} In these cases, the result has a type of F;
explicit conversion of the result is never required.  The accuracy required
in these cases is the same as that required for a multiplication F(P * Q) or
a division F(P / Q) obtained by interpreting the operand of the integer type
to have a fixed point type with a small of 1.0.

24   The accuracy of the result of a conversion from an integer or fixed
point type to a fixed point type, or from a fixed point type to an integer
type, is the same as that of a fixed point multiplication of the source value
by a fixed point operand having a small of 1.0 and a value of 1.0, as given
by the foregoing rules.  The result of a conversion from a floating point
type to a fixed point type shall belong to the close result set.  The result
of a conversion of a universal_real operand to a fixed point type shall
belong to the perfect result set.

25   The possibility of overflow in the result of a predefined arithmetic
operation or conversion yielding a result of a fixed point type T is
analogous to that for floating point types, except for being related to the
base range instead of the safe range.  {Overflow_Check [partial]} {check,
language-defined (Overflow_Check)} If all of the permitted results belong to
the base range of T, then the implementation shall deliver one of the
permitted results; otherwise,

   26  {Constraint_Error (raised by failure of run-time check)} if
       T'Machine_Overflows is True, the implementation shall either
       deliver one of the permitted results or raise Constraint_Error;

   27  if T'Machine_Overflows is False, the result is implementation
       defined.

 27.a   Implementation defined:  The result of a fixed point arithmetic
        operation in overflow situations, when the Machine_Overflows
        attribute of the result type is False.

{94-4774.e} {94-4889.k}


                         Inconsistencies With Ada 83

        27.b   {inconsistencies with Ada 83} Since the values of a fixed
        point type are now just the integer multiples of its small, the
        possibility of using extra bits available in the chosen
        representation for extra accuracy rather than for increasing the base
        range would appear to be removed, raising the possibility that some
        fixed point expressions will yield less accurate results than in Ada
        83.  However, this is partially offset by the ability of an
        implementation to choose a smaller default small than before.  Of
        course, if it does so for a type T then T'Small will have a different
        value than it previously had.

        27.c   The accuracy requirements in the case of incompatible smalls
        are relaxed to foster wider support for non-binary smalls.  If this
        relaxation is exploited for a type that was previously supported,
        lower accuracy could result; however, there is no particular
        incentive to exploit the relaxation in such a case.

                         Wording Changes From Ada 83

        27.d   The fixed point accuracy requirements are now expressed
        without reference to model or safe numbers, largely because the full
        generality of the former model was never exploited in the case of
        fixed point types (particularly in regard to operand perturbation).
        Although the new formulation in terms of perfect result sets and
        close result sets is still verbose, it can be seen to distill down to
        two cases:

         27.e  a case where the result must be the exact result, if the
               exact result is representable, or, if not, then either
               one of the adjacent values of the type (in some subcases
               only one of those adjacent values is allowed);

         27.f  a case where the accuracy is not specified by the
               language.



G.2.4 Accuracy Requirements for the Elementary Functions

1   In the strict mode, the performance of Numerics.Generic_Elementary_
Functions shall be as specified here.


                         Implementation Requirements

2   {result interval (for the evaluation of an elementary function)} {maximum
relative error (for the evaluation of an elementary function)} When an
exception is not raised, the result of evaluating a function in an instance
EF of Numerics.Generic_Elementary_Functions belongs to a result interval,
defined as the smallest model interval of EF.Float_Type that contains all the
values of the form f*(1.0+d), where f is the exact value of the corresponding
mathematical function at the given parameter values, d is a real number, and
|d| is less than or equal to the function's maximum relative error.
{Overflow_Check [partial]} {check, language-defined (Overflow_Check)} The
function delivers a value that belongs to the result interval when both of
its bounds belong to the safe range of EF.Float_Type; otherwise,

    3  {Constraint_Error (raised by failure of run-time check)} if
       EF.Float_Type'Machine_Overflows is True, the function either
       delivers a value that belongs to the result interval or raises
       Constraint_Error, signaling overflow;

    4  if EF.Float_Type'Machine_Overflows is False, the result is
       implementation defined.

 4.a    Implementation defined:  The result of an elementary function
        reference in overflow situations, when the Machine_Overflows
        attribute of the result type is False.

5   The maximum relative error exhibited by each function is as follows:

    6  2.0*EF.Float_Type'Model_Epsilon, in the case of the Sqrt, Sin,
       and Cos functions;

    7  4.0*EF.Float_Type'Model_Epsilon, in the case of the Log, Exp,
       Tan, Cot, and inverse trigonometric functions; and

    8  8.0*EF.Float_Type'Model_Epsilon, in the case of the forward and
       inverse hyperbolic functions.

9   The maximum relative error exhibited by the exponentiation operator,
which depends on the values of the operands, is
(4.0+|Right*log (Left)|/32.0)*EF.Float_Type'Model_Epsilon.

10   The maximum relative error given above applies throughout the domain of
the forward trigonometric functions when the Cycle parameter is specified.
{angle threshold} When the Cycle parameter is omitted, the maximum relative
error given above applies only when the absolute value of the angle parameter
X is less than or equal to some implementation-defined angle threshold, which
                                             Floor(EF.Float_Type'Machine_
shall be at least EF.Float_Type'Machine_Radix
Mantissa/2)
           .  Beyond the angle threshold, the accuracy of the forward
trigonometric functions is implementation defined.

        10.a   Implementation defined:  The value of the angle threshold,
        within which certain elementary functions, complex arithmetic
        operations, and complex elementary functions yield results conforming
        to a maximum relative error bound.

        10.b   Implementation defined:  The accuracy of certain elementary
        functions for parameters beyond the angle threshold.

        10.c   Implementation Note:  The angle threshold indirectly
        determines the amount of precision that the implementation has to
        maintain during argument reduction.

11   The prescribed results specified in A.5.1 for certain functions at
particular parameter values take precedence over the maximum relative error
bounds; effectively, they narrow to a single value the result interval
allowed by the maximum relative error bounds.  Additional rules with a
similar effect are given by the table below for the inverse trigonometric
functions, at particular parameter values for which the mathematical result
is possibly not a model number of EF.Float_Type (or is, indeed, even
transcendental).  In each table entry, the values of the parameters are such
that the result lies on the axis between two quadrants; the corresponding
accuracy rule, which takes precedence over the maximum relative error bounds,
is that the result interval is the model interval of EF.Float_Type associated
with the exact mathematical result given in the table.

12

13   The last line of the table is meant to apply when EF.Float_Type'Signed_
Zeros is False; the two lines just above it, when EF.Float_Type'Signed_Zeros
is True and the parameter Y has a zero value with the indicated sign.

14   The amount by which the result of an inverse trigonometric function is
allowed to spill over into a quadrant adjacent to the one corresponding to
the principal branch, as given in A.5.1, is limited.  The rule is that the
result belongs to the smallest model interval of EF.Float_Type that contains
both boundaries of the quadrant corresponding to the principal branch.  This
rule also takes precedence over the maximum relative error bounds,
effectively narrowing the result interval allowed by them.

15   Finally, the following specifications also take precedence over the
maximum relative error bounds:

   16  The absolute value of the result of the Sin, Cos, and Tanh
       functions never exceeds one.

-----------------------------------------------------------------------------
|                                                                           |
|             Tightly Approximated Elementary Function Results              |
|                                                                           |
|-------------------------------------------------------------------------- |
|                   |            |            |              |              |
|                   |            |            | Exact Result | Exact Result |
|                   |            |            |  when Cycle  |  when Cycle  |
|     Function      | Value of X | Value of Y |  Specified   |   Omitted    |
|                   |            |            |              |              |
|---------------------------------------------------------------------------|
|                   |            |            |              |              |
|      Arcsin       |    1.0     |    n.a.    |  Cycle/4.0   |    Pi/2.0    |
|                   |            |            |              |              |
|      Arcsin       |    -1.0    |    n.a.    |  -Cycle/4.0  |   -Pi/2.0    |
|                   |            |            |              |              |
|      Arccos       |    0.0     |    n.a.    |  Cycle/4.0   |    Pi/2.0    |
|                   |            |            |              |              |
|      Arccos       |    -1.0    |    n.a.    |  Cycle/2.0   |      Pi      |
|                   |            |            |              |              |
| Arctan and Arccot |    0.0     |  positive  |  Cycle/4.0   |    Pi/2.0    |
|                   |            |            |              |              |
| Arctan and Arccot |    0.0     |  negative  |  -Cycle/4.0  |   -Pi/2.0    |
|                   |            |            |              |              |
| Arctan and Arccot |  negative  |    +0.0    |  Cycle/2.0   |      Pi      |
|                   |            |            |              |              |
| Arctan and Arccot |  negative  |    -0.0    |  -Cycle/2.0  |     -Pi      |
|                   |            |            |              |              |
| Arctan and Arccot |  negative  |    0.0     |  Cycle/2.0   |      Pi      |
|                   |            |            |              |              |
-----------------------------------------------------------------------------


   17  The absolute value of the result of the Coth function is never
       less than one.

   18  The result of the Cosh function is never less than one.


                            Implementation Advice

19   The versions of the forward trigonometric functions without a Cycle
parameter should not be implemented by calling the corresponding version with
a Cycle parameter of 2.0*Numerics.Pi, since this will not provide the
required accuracy in some portions of the domain.  For the same reason, the
version of Log without a Base parameter should not be implemented by calling
the corresponding version with a Base parameter of Numerics.e.


                         Wording Changes From Ada 83

        19.a   The semantics of Numerics.Generic_Elementary_Functions differs
        from Generic_Elementary_Functions as defined in ISO/IEC DIS 11430
        (for Ada 83) in the following ways related to the accuracy specified
        for strict mode:

         19.b  The maximum relative error bounds use the Model_Epsilon
               attribute instead of the Base'Epsilon attribute.

         19.c  The accuracy requirements are expressed in terms of
               result intervals that are model intervals.  On the one
               hand, this facilitates the description of the required
               results in the presence of underflow; on the other hand,
               it slightly relaxes the requirements expressed in ISO/IEC
               DIS 11430.



G.2.5 Performance Requirements for Random Number Generation

1   In the strict mode, the performance of Numerics.Float_Random and
Numerics.Discrete_Random shall be as specified here.


                         Implementation Requirements

2   Two different calls to the time-dependent Reset procedure shall reset the
generator to different states, provided that the calls are separated in time
by at least one second and not more than fifty years.

3   The implementation's representations of generator states and its
algorithms for generating random numbers shall yield a period of at least
 31
2  -2; much longer periods are desirable but not required.

4   The implementations of Numerics.Float_Random.Random and Numerics.-
Discrete_Random.Random shall pass at least 85% of the individual trials in a
suite of statistical tests.  For Numerics.Float_Random, the tests are applied
directly to the floating point values generated (i.e., they are not converted
to integers first), while for Numerics.Discrete_Random they are applied to
the generated values of various discrete types.  Each test suite performs 6
different tests, with each test repeated 10 times, yielding a total of 60
individual trials.  An individual trial is deemed to pass if the chi-square
value (or other statistic) calculated for the observed counts or distribution
falls within the range of values corresponding to the 2.5 and 97.5 percentage
points for the relevant degrees of freedom (i.e., it shall be neither too
high nor too low).  For the purpose of determining the degrees of freedom,
measurement categories are combined whenever the expected counts are fewer
than 5.

        4.a   Implementation Note:  In the floating point random number test
        suite, the generator is reset to a time-dependent state at the
        beginning of the run.  The test suite incorporates the following
        tests, adapted from D. E. Knuth, The Art of Computer Programming,
        vol. 2: Seminumerical Algorithms.  In the descriptions below, the
        given number of degrees of freedom is the number before reduction due
        to any necessary combination of measurement categories with small
        expected counts; it is one less than the number of measurement
        categories.

          4.b  Proportional Distribution Test (a variant of the
               Equidistribution Test).  The interval 0.0 .. 1.0 is
               partitioned into K subintervals.  K is chosen randomly
               between 4 and 25 for each repetition of the test, along
               with the boundaries of the subintervals (subject to the
               constraint that at least 2 of the subintervals have a
               width of 0.001 or more).  5000 random floating point
               numbers are generated.  The counts of random numbers
               falling into each subinterval are tallied and compared
               with the expected counts, which are proportional to the
               widths of the subintervals.  The number of degrees of
               freedom for the chi-square test is K-1.

          4.c  Gap Test.  The bounds of a range A .. B, with
               0.0<=A<B<=1.0, are chosen randomly for each repetition of
               the test, subject to the constraint that 0.2<=B-A<=0.6.
               Random floating point numbers are generated until 5000
               falling into the range A .. B have been encountered.
               Each of these 5000 is preceded by a ``gap'' (of length
               greater than or equal to 0) of consecutive random numbers
               not falling into the range A .. B.  The counts of gaps of
               each length from 0 to 15, and of all lengths greater than
               15 lumped together, are tallied and compared with the
               expected counts.  Let P=B-A.  The probability that a gap
                                         L
               has a length of L is (1-P) *P for L<=15, while the
               probability that a gap has a length of 16 or more is
                    16
               (1-P)  .  The number of degrees of freedom for the
               chi-square test is 16.

          4.d  Permutation Test.  5000 tuples of 4 different random
               floating point numbers are generated.  (An entire 4-tuple
               is discarded in the unlikely event that it contains any
               two exactly equal components.)  The counts of each of the
               4!=24 possible relative orderings of the components of
               the 4-tuples are tallied and compared with the expected
               counts.  Each of the possible relative orderings has an
               equal probability.  The number of degrees of freedom for
               the chi-square test is 23.

          4.e  Increasing-Runs Test.  Random floating point numbers are
               generated until 5000 increasing runs have been observed.
               An ``increasing run'' is a sequence of random numbers in
               strictly increasing order; it is followed by a random
               number that is strictly smaller than the preceding random
               number.  (A run under construction is entirely discarded
               in the unlikely event that one random number is followed
               immediately by an exactly equal random number.)  The
               decreasing random number that follows an increasing run
               is discarded and not included with the next increasing
               run.  The counts of increasing runs of each length from 1
               to 4, and of all lengths greater than 4 lumped together,
               are tallied and compared with the expected counts.  The
               probability that an increasing run has a length of L is
               1/L!-1/(L+1)! for L<=4, while the probability that an
               increasing run has a length of 5 or more is 1/5!.  The
               number of degrees of freedom for the chi-square test is
               4.

          4.f  Decreasing-Runs Test.  The test is similar to the
               Increasing Runs Test, but with decreasing runs.

          4.g  Maximum-of-t Test (with t=5).  5000 tuples of 5 random
               floating point numbers are generated.  The maximum of the
               components of each 5-tuple is determined and raised to
               the 5th power.  The uniformity of the resulting values
               over the range 0.0 .. 1.0 is tested as in the
               Proportional Distribution Test.

        4.h   Implementation Note:  In the discrete random number test suite,
        Numerics.Discrete_Random is instantiated as described below.  The
        generator is reset to a time-dependent state after each
        instantiation.  The test suite incorporates the following tests,
        adapted from D. E. Knuth (op. cit.) and other sources.  The given
        number of degrees of freedom for the chi-square test is reduced by
        any necessary combination of measurement categories with small
        expected counts, as described above.

          4.i  Equidistribution Test.  In each repetition of the test, a
               number R between 2 and 30 is chosen randomly, and
               Numerics.Discrete_Random is instantiated with an integer
               subtype whose range is 1 .. R.  5000 integers are
               generated randomly from this range.  The counts of
               occurrences of each integer in the range are tallied and
               compared with the expected counts, which have equal
               probabilities.  The number of degrees of freedom for the
               chi-square test is R-1.

          4.j  Simplified Poker Test.  Numerics.Discrete_Random is
               instantiated once with an enumeration subtype represent-
               ing the 13 denominations (Two through Ten, Jack, Queen,
               King, and Ace) of an infinite deck of playing cards.
               2000 ``poker'' hands (5-tuples of values of this subtype)
               are generated randomly.  The counts of hands containing
               exactly K different denominations (1<=K<=5) are tallied
               and compared with the expected counts.  The probability
               that a hand contains exactly K different denominations is
               given by a formula in Knuth.  The number of degrees of
               freedom for the chi-square test is 4.

          4.k  Coupon Collector's Test.  Numerics.Discrete_Random is
               instantiated in each repetition of the test with an
               integer subtype whose range is 1 .. R, where R varies
               systematically from 2 to 11.  Integers are generated
               randomly from this range until each value in the range
               has occurred, and the number K of integers generated is
               recorded.  This constitutes a ``coupon collector's
               segment'' of length K.  2000 such segments are generated.
               The counts of segments of each length from R to R+29, and
               of all lengths greater than R+29 lumped together, are
               tallied and compared with the expected counts.  The
               probability that a segment has any given length is given
               by formulas in Knuth.  The number of degrees of freedom
               for the chi-square test is 30.

          4.l  Craps Test (Lengths of Games).  Numerics.Discrete_Random
               is instantiated once with an integer subtype whose range
               is 1 .. 6 (representing the six numbers on a die).  5000
               craps games are played, and their lengths are recorded.
               (The length of a craps game is the number of rolls of the
               pair of dice required to produce a win or a loss.  A game
               is won on the first roll if the dice show 7 or 11; it is
               lost if they show 2, 3, or 12.  If the dice show some
               other sum on the first roll, it is called the point, and
               the game is won if and only if the point is rolled again
               before a 7 is rolled.)  The counts of games of each
               length from 1 to 18, and of all lengths greater than 18
               lumped together, are tallied and compared with the
               expected counts.  For 2<=S<=12, let D  be the probability
                                                    S
               that a roll of a pair of dice shows the sum S, and let
                                   L-2
               Q (L)=D *(1-(D +D ))   *(D +D ).  Then, the probability
                S     S      S  7        S  7
               that a game has a length of 1 is D +D  +D +D +D   and,
                                                 7  11  2  3  12
               for L>1, the probability that a game has a length of L is
               Q (L)+Q (L)+Q (L)+Q (L)+Q (L)+Q  (L).  The number of
                4     5     6     8     9     10
               degrees of freedom for the chi-square test is 18.

          4.m  Craps Test (Lengths of Passes).  This test is similar to
               the last, but enough craps games are played for 3000
               losses to occur.  A string of wins followed by a loss is
               called a pass, and its length is the number of wins
               preceding the loss.  The counts of passes of each length
               from 0 to 7, and of all lengths greater than 7 lumped
               together, are tallied and compared with the expected
               counts.  For L>=0, the probability that a pass has a
                               L
               length of L is W *(1-W), where W, the probability that a
               game ends in a win, is 244.0/495.0.  The number of
               degrees of freedom for the chi-square test is 8.

          4.n  Collision Test.  Numerics.Discrete_Random is instantiated
               once with an integer or enumeration type representing
               binary bits.  15 successive calls on the Random function
               are used to obtain the bits of a 15-bit binary integer
               between 0 and 32767.  3000 such integers are generated,
               and the number of collisions (integers previously
               generated) is counted and compared with the expected
               count.  A chi-square test is not used to assess the
               number of collisions; rather, the limits on the number of
               collisions, corresponding to the 2.5 and 97.5 percentage
               points, are (from formulas in Knuth) 112 and 154.  The
               test passes if and only if the number of collisions is in
               this range.



G.2.6 Accuracy Requirements for Complex Arithmetic

1   In the strict mode, the performance of Numerics.Generic_Complex_Types and
Numerics.Generic_Complex_Elementary_Functions shall be as specified here.


                         Implementation Requirements

2   When an exception is not raised, the result of evaluating a real function
of an instance CT of Numerics.Generic_Complex_Types (i.e., a function that
yields a value of subtype CT.Real'Base or CT.Imaginary) belongs to a result
interval defined as for a real elementary function (see G.2.4).

3   {result interval (for a component of the result of evaluating a complex
function)} When an exception is not raised, each component of the result of
evaluating a complex function of such an instance, or of an instance of
Numerics.Generic_Complex_Elementary_Functions obtained by instantiating the
latter with CT (i.e., a function that yields a value of subtype CT.Complex),
also belongs to a result interval.  The result intervals for the components
of the result are either defined by a maximum relative error bound or by a
maximum box error bound.  {maximum relative error (for a component of the
result of evaluating a complex function)} When the result interval for the
real (resp., imaginary) component is defined by maximum relative error, it is
defined as for that of a real function, relative to the exact value of the
real (resp., imaginary) part of the result of the corresponding mathematical
function.

        3.a   Discussion:  The maximum relative error could be specified
        separately for each component, but we do not take advantage of that
        freedom here.

{maximum box error (for a component of the result of evaluating a complex
function)} When defined by maximum box error, the result interval for a
component of the result is the smallest model interval of CT.Real that
contains all the values of the corresponding part of f*(1.0+d), where f is
the exact complex value of the corresponding mathematical function at the
given parameter values, d is complex, and |d| is less than or equal to the
given maximum box error.

        3.b   Discussion:  Note that f*(1.0+d) defines a small circular
        region of the complex plane centered at f, and the result intervals
        for the real and imaginary components of the result define a small
        rectangular box containing that circle.

        3.c   Reason:  Box error is used when the computation of the result
        risks loss of significance in a component due to cancellation.

        3.d   Ramification:  The components of a complex function that
        exhibits bounded relative error in each component have to have the
        correct sign.  In contrast, one of the components of a complex
        function that exhibits bounded box error may have the wrong sign,
        since the dimensions of the box containing the result are
        proportional to the modulus of the mathematical result and not to
        either component of the mathematical result individually.  Thus, for
        example, the box containing the computed result of a complex function
        whose mathematical result has a large modulus but lies very close to
        the imaginary axis might well straddle that axis, allowing the real
        component of the computed result to have the wrong sign.  In this
        case, the distance between the computed result and the mathematical
        result is, nevertheless, a small fraction of the modulus of the
        mathematical result.

{Overflow_Check [partial]} {check, language-defined (Overflow_Check)} The
function delivers a value that belongs to the result interval (or a value
both of whose components belong to their respective result intervals) when
both bounds of the result interval(s) belong to the safe range of CT.Real;
otherwise,

    4  {Constraint_Error (raised by failure of run-time check)} if
       CT.Real'Machine_Overflows is True, the function either delivers a
       value that belongs to the result interval (or a value both of
       whose components belong to their respective result intervals) or
       raises Constraint_Error, signaling overflow;

    5  if CT.Real'Machine_Overflows is False, the result is implemen-
       tation defined.

 5.a    Implementation defined:  The result of a complex arithmetic
        operation or complex elementary function reference in overflow
        situations, when the Machine_Overflows attribute of the
        corresponding real type is False.

6   The error bounds for particular complex functions are tabulated below.
In the table, the error bound is given as the coefficient of CT.Real'Model_
Epsilon.

7

8   The maximum relative error given above applies throughout the domain of
the Compose_From_Polar function when the Cycle parameter is specified.  When
the Cycle parameter is omitted, the maximum relative error applies only when
the absolute value of the parameter Argument is less than or equal to the
angle threshold (see G.2.4).  For the Exp function, and for the forward
hyperbolic (resp., trigonometric) functions, the maximum relative error given
above likewise applies only when the absolute value of the imaginary (resp.,
real) component of the parameter X (or the absolute value of the parameter
itself, in the case of the Exp function with a parameter of pure-imaginary
type) is less than or equal to the angle threshold.  For larger angles, the
accuracy is implementation defined.

        8.a   Implementation defined:  The accuracy of certain complex
        arithmetic operations and certain complex elementary functions for
        parameters (or components thereof) beyond the angle threshold.

9   The prescribed results specified in G.1.2 for certain functions at
particular parameter values take precedence over the error bounds;
effectively, they narrow to a single value the result interval allowed by the
error bounds for a component of the result.  Additional rules with a similar
effect are given below for certain inverse trigonometric and inverse
hyperbolic functions, at particular parameter values for which a component of
the mathematical result is transcendental.  In each case, the accuracy rule,
which takes precedence over the error bounds, is that the result interval for
the stated result component is the model interval of CT.Real associated with
the component's exact mathematical value.  The cases in question are as
follows:

 ---------------------------------------------------------------------------
 |                                                                         |
 |              Error Bounds for Particular Complex Functions              |
 |                                                                         |
 |------------------------------------------------------------------------ |
 |                             |           |                 |             |
 |                             | Nature of |    Nature of    |             |
 |    Function or Operator     |  Result   |      Bound      | Error Bound |
 |                             |           |                 |             |
 |-------------------------------------------------------------------------|
 |                             |           |                 |             |
 |           Modulus           |   real    | max. rel. error |     3.0     |
 |                             |           |                 |             |
 |          Argument           |   real    | max. rel. error |     4.0     |
 |                             |           |                 |             |
 |     Compose_From_Polar      |  complex  | max. rel. error |     3.0     |
 |                             |           |                 |             |
 | "*" (both operands complex) |  complex  | max. box error  |     5.0     |
 |                             |           |                 |             |
 | "/" (right operand complex) |  complex  | max. box error  |    13.0     |
 |                             |           |                 |             |
 |            Sqrt             |  complex  | max. rel. error |     6.0     |
 |                             |           |                 |             |
 |             Log             |  complex  | max. box error  |    13.0     |
 |                             |           |                 |             |
 |   Exp (complex parameter)   |  complex  | max. rel. error |     7.0     |
 |                             |           |                 |             |
 |  Exp (imaginary parameter)  |  complex  | max. rel. error |     2.0     |
 |                             |           |                 |             |
 |  Sin, Cos, Sinh, and Cosh   |  complex  | max. rel. error |    11.0     |
 |                             |           |                 |             |
 |  Tan, Cot, Tanh, and Coth   |  complex  | max. rel. error |    35.0     |
 |                             |           |                 |             |
 |    inverse trigonometric    |  complex  | max. rel. error |    14.0     |
 |                             |           |                 |             |
 |     inverse hyperbolic      |  complex  | max. rel. error |    14.0     |
 |                             |           |                 |             |
 ---------------------------------------------------------------------------

   10  When the parameter X has the value zero, the real (resp.,
       imaginary) component of the result of the Arccot (resp., Arccoth)
       function is in the model interval of CT.Real associated with the
       value Pi/2.0.

   11  When the parameter X has the value one, the real component of the
       result of the Arcsin function is in the model interval of CT.Real
       associated with the value Pi/2.0.

   12  When the parameter X has the value -1.0, the real component of
       the result of the Arcsin (resp., Arccos) function is in the model
       interval of CT.Real associated with the value -Pi/2.0 (resp.,
       Pi).

        12.a   Discussion:  It is possible to give many other prescribed
        results in which a component of the parameter is restricted to a
        similar model interval when the parameter X is appropriately
        restricted to an easily testable portion of the domain.  We follow
        the proposed ISO/IEC standard for Generic_Complex_Elementary_
        Functions (for Ada 83) in not doing so, however.

13   The amount by which a component of the result of an inverse
trigonometric or inverse hyperbolic function is allowed to spill over into a
quadrant adjacent to the one corresponding to the principal branch, as given
in G.1.2, is limited.  The rule is that the result belongs to the smallest
model interval of CT.Real that contains both boundaries of the quadrant
corresponding to the principal branch.  This rule also takes precedence to
the maximum error bounds, effectively narrowing the result interval allowed
by them.

14   Finally, the results allowed by the error bounds are narrowed by one
further rule: The absolute value of each component of the result of the Exp
function, for a pure-imaginary parameter, never exceeds one.


                            Implementation Advice

15   The version of the Compose_From_Polar function without a Cycle parameter
should not be implemented by calling the corresponding version with a Cycle
parameter of 2.0*Numerics.Pi, since this will not provide the required
accuracy in some portions of the domain.


                         Wording Changes From Ada 83

        15.a   The semantics of Numerics.Generic_Complex_Types and Numerics.-
        Generic_Complex_Elementary_Functions differs from Generic_Complex_
        Types and Generic_Complex_Elementary_Functions as defined in ISO/IEC
        CDs 13813 and 13814 (for Ada 83) in ways analogous to those
        identified for the elementary functions in G.2.4.  In addition, we do
        not generally specify the signs of zero results (or result
        components), although those proposed standards do.



                                   Annex H
                                 (normative)


                             Safety and Security



1   {safety-critical systems} {secure systems} This Annex addresses
requirements for systems that are safety critical or have security
constraints.  It provides facilities and specifies documentation requirements
that relate to several needs:

    2  Understanding program execution;

    3  Reviewing object code;

    4  Restricting language constructs whose usage might complicate the
       demonstration of program correctness

Execution understandability is supported by pragma Normalize_Scalars, and
also by requirements for the implementation to document the effect of a
program in the presence of a bounded error or where the language rules leave
the effect unspecified.  {unspecified [partial]}

5   The pragmas Reviewable and Restrictions relate to the other requirements
addressed by this Annex.


     NOTES
6    (1) The Valid attribute (see 13.9.2) is also useful in addressing these
     needs, to avoid problems that could otherwise arise from scalars that
     have values outside their declared range constraints.


                            Extensions to Ada 83

        6.a   {extensions to Ada 83} This Annex is new to Ada 9X.



H.1 Pragma Normalize_Scalars

1   This pragma ensures that an otherwise uninitialized scalar object is set
to a predictable value, but out of range if possible.

        1.a   Discussion:  The goal of the pragma is to reduce the impact of
        a bounded error that results from a reference to an uninitialized
        scalar object, by having such a reference violate a range check and
        thus raise Constraint_Error.


                                   Syntax

    2   The form of a pragma Normalize_Scalars is as follows:


3     pragma Normalize_Scalars;


                           Post-Compilation Rules

4   {post-compilation rules} {configuration pragma [Normalize_Scalars]}
{pragma, configuration [Normalize_Scalars]} Pragma Normalize_Scalars is a
configuration pragma.  It applies to all compilation_units included in a
partition.


                         Documentation Requirements

5   {documentation requirements} If a pragma Normalize_Scalars applies, the
implementation shall document the implicit initial value for scalar subtypes,
and shall identify each case in which such a value is used and is not an
invalid representation.

        5.a   To be honest:  It's slightly inaccurate to say that the value
        is a representation, but the point should be clear anyway.


                            Implementation Advice

6   Whenever possible, the implicit initial value for a scalar subtype should
be an invalid representation (see 13.9.1).


     NOTES
7    (2) The initialization requirement applies to uninitialized scalar
     objects that are subcomponents of composite objects, to allocated
     objects, and to stand-alone objects.  It also applies to scalar out
     parameters.  Scalar subcomponents of composite out parameters are
     initialized to the corresponding part of the actual, by virtue of 6.4.1.

8    (3) The initialization requirement does not apply to a scalar for which
     pragma Import has been specified, since initialization of an imported
     object is performed solely by the foreign language environment (see
     B.1).

9    (4) The use of pragma Normalize_Scalars in conjunction with Pragma
     Restrictions(No_Exceptions) may result in erroneous execution (see H.4).
H.2 Documentation of Implementation Decisions

                         Documentation Requirements

1   {documentation requirements} {unspecified [partial]} The implementation
shall document the range of effects for each situation that the language
rules identify as either a bounded error or as having an unspecified effect.
If the implementation can constrain the effects of erroneous execution for a
given construct, then it shall document such constraints.  [The documentation
might be provided either independently of any compilation unit or partition,
or as part of an annotated listing for a given unit or partition.  See also
1.1.3, and 1.1.2.]

        1.a   Implementation defined:  Information regarding bounded errors
        and erroneous execution.


     NOTES
2    (5) Among the situations to be documented are the conventions chosen for
     parameter passing, the methods used for the management of run-time
     storage, and the method used to evaluate numeric expressions if this
     involves extended range or extra precision.



H.3 Reviewable Object Code

1   Object code review and validation are supported by pragmas Reviewable and
Inspection_Point.



H.3.1 Pragma Reviewable

1   This pragma directs the implementation to provide information to
facilitate analysis and review of a program's object code, in particular to
allow determination of execution time and storage usage and to identify the
correspondence between the source and object programs.


                                   Syntax

    2   The form of a pragma Reviewable is as follows:


3     pragma Reviewable;


                           Post-Compilation Rules

4   {post-compilation rules} {configuration pragma [Reviewable]} {pragma,
configuration [Reviewable]} Pragma Reviewable is a configuration pragma.  It
applies to all compilation_units included in a partition.


                         Implementation Requirements

5   The implementation shall provide the following information for any
compilation unit to which such a pragma applies:

    6  Where compiler-generated run-time checks remain;

    7  An identification of any construct with a language-defined check
       that is recognized prior to run time as certain to fail if
       executed (even if the generation of run-time checks has been
       suppressed);

    8  For each reference to a scalar object, an identification of the
       reference as either ``known to be initialized,'' or ``possibly
       uninitialized,'' independent of whether pragma Normalize_Scalars
       applies;

    9  Where run-time support routines are implicitly invoked;

   10  An object code listing, including:

          11  Machine instructions, with relative offsets;

          12  Where each data object is stored during its lifetime;

          13  Correspondence with the source program, including an
              identification of the code produced per declaration and
              per statement.

   14  An identification of each construct for which the implementation
       detects the possibility of erroneous execution;

   15  For each subprogram, block, task, or other construct implemented
       by reserving and subsequently freeing an area on a run-time
       stack, an identification of the length of the fixed-size portion
       of the area and an indication of whether the non-fixed size
       portion is reserved on the stack or in a dynamically-managed
       storage region.

16   The implementation shall provide the following information for any
partition to which the pragma applies:

   17  An object code listing of the entire partition, including
       initialization and finalization code as well as run-time system
       components, and with an identification of those instructions and
       data that will be relocated at load time;

 17.a   Discussion:  The object code listing should enable a validator
        to estimate upper bounds for the time taken by critical parts of
        a program.  Similarly, by an analysis of the entire partition,
        it should be possible to ensure that the storage requirements
        are suitably bounded, assuming that the partition was written in
        an appropriate manner.

   18  A description of the run-time model relevant to the partition.


The implementation shall provide control- and data-flow information, both
within each compilation unit and across the compilation units of the
partition.

                            Implementation Advice

19   The implementation should provide the above information in both a
human-readable and machine-readable form, and should document the latter so
as to ease further processing by automated tools.

20   Object code listings should be provided both in a symbolic format and
also in an appropriate numeric format (such as hexadecimal or octal).


     NOTES
21   (6) The order of elaboration of library units will be documented even in
     the absence of pragma Reviewable (see 10.2).  {94-4898.b}


        21.a   Discussion:  There might be some interactions between pragma
        Reviewable and compiler optimizations.  For example, an
        implementation may disable some optimizations when pragma Reviewable
        is in force if it would be overly complicated to provide the detailed
        information to allow review of the optimized object code.  See also
        pragma Optimize (2.8).



H.3.2 Pragma Inspection_Point

1   An occurrence of a pragma Inspection_Point identifies a set of objects
each of whose values is to be available at the point(s) during program
execution corresponding to the position of the pragma in the compilation
unit.  The purpose of such a pragma is to facilitate code validation.


                                   Syntax

    2   The form of a pragma Inspection_Point is as follows:


3     pragma Inspection_Point[(object_name {, object_name})];


                               Legality Rules

4   A pragma Inspection_Point is allowed wherever a declarative_item or
statement is allowed.  Each object_name shall statically denote the
declaration of an object.


                              Static Semantics

5   {inspection point} An inspection point is a point in the object code
corresponding to the occurrence of a pragma Inspection_Point in the
compilation unit.

        5.a   Ramification:  If a pragma Inspection_Point is in an in-lined
        subprogram, there might be numerous inspection points in the object
        code corresponding to the single occurrence of the pragma in the
        source; similar considerations apply if such a pragma is in a
        generic, or in a loop that has been ``unrolled'' by an optimizer.

{inspectable object} An object is inspectable at an inspection point if the
corresponding pragma Inspection_Point either has an argument denoting that
object, or has no arguments.


                              Dynamic Semantics

6   Execution of a pragma Inspection_Point has no effect.


                         Implementation Requirements

7   Reaching an inspection point is an external interaction with respect to
the values of the inspectable objects at that point (see 1.1.3).

        7.a   Ramification:  The compiler is inhibited from moving an
        assignment to an inspectable variable past an inspection point for
        that variable.  On the other hand, the evaluation of an expression
        that might raise an exception may be moved past an inspection point
        (see 11.6).


                         Documentation Requirements
8   {documentation requirements} For each inspection point, the implemen-
tation shall identify a mapping between each inspectable object and the
machine resources (such as memory locations or registers) from which the
object's value can be obtained.

        8.a   Implementation defined:  Implementation-defined aspects of
        pragma Inspection_Point.


     NOTES
9    (7) The implementation is not allowed to perform ``dead store
     elimination'' on the last assignment to a variable prior to a point
     where the variable is inspectable.  Thus an inspection point has the
     effect of an implicit reference to each of its inspectable objects.

10   (8) Inspection points are useful in maintaining a correspondence between
     the state of the program in source code terms, and the machine state
     during the program's execution.  Assertions about the values of program
     objects can be tested in machine terms at inspection points.  Object
     code between inspection points can be processed by automated tools to
     verify programs mechanically.

11   (9) The identification of the mapping from source program objects to
     machine resources is allowed to be in the form of an annotated object
     listing, in human-readable or tool-processable form.



H.4 Safety and Security Restrictions

1   This clause defines restrictions that can be used with pragma
Restrictions (see 13.12); these facilitate the demonstration of program
correctness by allowing tailored versions of the run-time system.


                              Static Semantics

2   The following restrictions, the same as in D.7, apply in this Annex:  No_
Task_Hierarchy, No_Abort_Statement, No_Implicit_Heap_Allocation, Max_Task_
Entries is 0, Max_Asynchronous_Select_Nesting is 0, and Max_Tasks is 0.  [The
last three restrictions are checked prior to program execution.]

3   The following additional restrictions apply in this Annex.

4   Tasking-related restriction:

5   {Restrictions (No_Protected_Types)} No_Protected_Types
                There are no declarations of protected types or protected
                objects.

6   Memory-management related restrictions:

7   {Restrictions (No_Allocators)} No_Allocators
                There are no occurrences of an allocator.

8   {Restrictions (No_Local_Allocators)} No_Local_Allocators
                Allocators are prohibited in subprograms, generic sub-
                programs, tasks, and entry bodies; instantiations of generic
                packages are also prohibited in these contexts.

8.a     Ramification:  Thus allocators are permitted only in expressions
        whose evaluation can only be performed before the main subprogram is
        invoked.

8.b     Reason:  The reason for the prohibition against instantiations of
        generic packages is to avoid contract model violations.  An
        alternative would be to prohibit allocators from generic packages,
        but it seems preferable to allow generality on the defining side and
        then place the restrictions on the usage (instantiation), rather than
        inhibiting what can be in the generic while liberalizing where they
        can be instantiated.

9   {Restrictions (No_Unchecked_Deallocation)} No_Unchecked_Deal-
                location
                Semantic dependence on Unchecked_Deallocation is not allowed.

10  Immediate_Reclamation
                Except for storage occupied by objects created by allocators
                and not deallocated via unchecked deallocation, any storage
                reserved at run time for an object is immediately reclaimed
                when the object no longer exists.  {Restrictions (Immediate_
                Reclamation)}

11  Exception-related restriction:

12  {Restrictions (No_Exceptions)} No_Exceptions
                Raise_statements and exception_handlers are not allowed.  No
                language-defined run-time checks are generated; however, a
                run-time check performed automatically by the hardware is
                permitted.

13  Other restrictions:

14  {Restrictions (No_Floating_Point)} No_Floating_Point
                Uses of predefined floating point types and operations, and
                declarations of new floating point types, are not allowed.

15  {Restrictions (No_Fixed_Point)} No_Fixed_Point
                Uses of predefined fixed point types and operations, and
                declarations of new fixed point types, are not allowed.

16  {Restrictions (No_Unchecked_Conversion)} No_Unchecked_Conver-
                sion
                Semantic dependence on the predefined generic Unchecked_
                Conversion is not allowed.

17  No_Access_Subprograms
                The declaration of access-to-subprogram types is not allowed.
                {Restrictions (No_Access_Subprograms)}

18  {Restrictions (No_Unchecked_Access)} No_Unchecked_Access
                The Unchecked_Access attribute is not allowed.

19  {Restrictions (No_Dispatch)} No_Dispatch
                Occurrences of T'Class are not allowed, for any (tagged)
                subtype T.

20  {Restrictions (No_IO)} No_IO
                Semantic dependence on any of the library units
                Sequential_IO, Direct_IO, Text_IO, Wide_Text_IO, or Stream_IO
                is not allowed.

21  {Restrictions (No_Delay)} No_Delay
                Delay_Statements and semantic dependence on package Calendar
                are not allowed.

21.a    Ramification:  This implies that delay_alternatives in a select_
        statement are prohibited.

22  {Restrictions (No_Recursion)} No_Recursion
                As part of the execution of a subprogram, the same subprogram
                is not invoked.

23  {Restrictions (No_Reentrancy)} No_Reentrancy
                During the execution of a subprogram by a task, no other task
                invokes the same subprogram.


                         Implementation Requirements

24   If an implementation supports pragma Restrictions for a particular
argument, then except for the restrictions No_Unchecked_Deallocation, No_
Unchecked_Conversion, No_Access_Subprograms, and No_Unchecked_Access, the
associated restriction applies to the run-time system.

        24.a   Reason:  Permission is granted for the run-time system to use
        the specified otherwise-restricted features, since the use of these
        features may simplify the run-time system by allowing more of it to
        be written in Ada.


                         Documentation Requirements

25   {documentation requirements} If a pragma Restrictions(No_Exceptions) is
specified, the implementation shall document the effects of all constructs
where language-defined checks are still performed automatically (for example,
an overflow check performed by the processor).

        25.a   Implementation defined:  Implementation-defined aspects of
        pragma Restrictions.


                             Erroneous Execution

26   {erroneous execution} Program execution is erroneous if pragma
Restrictions(No_Exceptions) has been specified and the conditions arise under
which a generated language-defined run-time check would fail.

27   Program execution is erroneous if pragma Restrictions(No_Recursion) has
been specified and a subprogram is invoked as part of its own execution, or
if pragma Restrictions(No_Reentrancy) has been specified and during the
execution of a subprogram by a task, another task invokes the same
subprogram.  {94-4859.c}


        27.a   Implementation defined:  Any restrictions on pragma
        Restrictions.



                                   Annex J
                                 (normative)


                             Obsolescent Features



1   [{obsolescent feature} This Annex contains descriptions of features of
the language whose functionality is largely redundant with other features
defined by this International Standard.  Use of these features is not
recommended in newly written programs.]

        1.a   Ramification:  These features are still part of the language,
        and have to be implemented by conforming implementations.  The
        primary reason for putting these descriptions here is to get
        redundant features out of the way of most readers.  The designers of
        the next version of Ada after Ada 9X will have to assess whether or
        not it makes sense to drop these features from the language.
                         Wording Changes From Ada 83

        1.b   The following features have been removed from the language,
        rather than declared to be obsolescent:

          1.c  The package Low_Level_IO (see A.6).

          1.d  The Epsilon, Mantissa, Emax, Small, Large, Safe_Emax,
               Safe_Small, and Safe_Large attributes of floating point
               types (see A.5.3).

          1.e  The pragma Interface (see B.1).

          1.f  The pragmas System_Name, Storage_Unit, and Memory_Size
               (see 13.7).

          1.g  The pragma Shared (see C.6).

        1.h   Implementations can continue to support the above features for
        upward compatibility.



J.1 Renamings of Ada 83 Library Units

                              Static Semantics

1   The following library_unit_renaming_declarations exist:

2   with Ada.Unchecked_Conversion;
    generic function Unchecked_Conversion renames Ada.Unchecked_Conversion;

3   with Ada.Unchecked_Deallocation;
    generic procedure Unchecked_Deallocation renames Ada.Unchecked_Deallocation;

4   with Ada.Sequential_IO;
    generic package Sequential_IO renames Ada.Sequential_IO;

5   with Ada.Direct_IO;
    generic package Direct_IO renames Ada.Direct_IO;

6   with Ada.Text_IO;
    package Text_IO renames Ada.Text_IO;

7   with Ada.IO_Exceptions;
    package IO_Exceptions renames Ada.IO_Exceptions;

8   with Ada.Calendar;
    package Calendar renames Ada.Calendar;

9   with System.Machine_Code;
    package Machine_Code renames System.Machine_Code; -- If supported.


                         Implementation Requirements

10   The implementation shall allow the user to replace these renamings.



J.2 Allowed Replacements of Characters

                                   Syntax

    1   The following replacements are allowed for the vertical line, number
    sign, and quotation mark characters:

        2  A vertical line character (|) can be replaced by an
           exclamation mark (!) where used as a delimiter.

        3  The number sign characters (#) of a based_literal can be
           replaced by colons (:) provided that the replacement is done
           for both occurrences.

 3.a    To be honest:  The intent is that such a replacement works in
        the Value and Wide_Value attributes, and in the Get procedures
        of Text_IO, so that things like ``16:.123:'' is acceptable.

        4  The quotation marks (") used as string brackets at both ends
           of a string literal can be replaced by percent signs (%)
           provided that the enclosed sequence of characters contains no
           quotation mark, and provided that both string brackets are
           replaced.  Any percent sign within the sequence of characters
           shall then be doubled and each such doubled percent sign is
           interpreted as a single percent sign character value.

    5   These replacements do not change the meaning of the program.

        5.a   Reason:  The original purpose of this feature was to support
        hardware (for example, teletype machines) that has long been
        obsolete.  The feature is no longer necessary for that reason.
        Another use of the feature has been to replace the vertical line
        character (|) when using certain hardware that treats that character
        as a (non-English) letter.  The feature is no longer necessary for
        that reason, either, since Ada 9X has full support for international
        character sets.  Therefore, we believe this feature is no longer
        necessary.

        5.b   Users of equipment that still uses | to represent a letter will
        continue to do so.  Perhaps by next the time Ada is revised, such
        equipment will no longer be in use.

        5.c   Note that it was never legal to use this feature as a
        convenient method of including double quotes in a string without
        doubling them -- the string literal:

5.d         %"This is quoted."%

        5.e   is not legal in Ada 83, nor will it be in Ada 9X.  One has to
        write:

5.f         """This is quoted."""



J.3 Reduced Accuracy Subtypes

1   A digits_constraint may be used to define a floating point subtype with a
new value for its requested decimal precision, as reflected by its Digits
attribute.  Similarly, a delta_constraint may be used to define an ordinary
fixed point subtype with a new value for its delta, as reflected by its Delta
attribute.

        1.a   Discussion:  It might be more direct to make these attributes
        specifiable via an attribute_definition_clause, and eliminate the
        syntax for these _constraints.


                                   Syntax

2   delta_constraint ::= delta static_expression [range_constraint]


                            Name Resolution Rules

3   {expected type [delta_constraint expression]} The expression of a delta_
constraint is expected to be of any real type.  {94-4774.f}


                               Legality Rules

4   The expression of a delta_constraint shall be static.

5   For a subtype_indication with a delta_constraint, the subtype_mark shall
denote an ordinary fixed point subtype.

6   {notwithstanding} For a subtype_indication with a digits_constraint, the
subtype_mark shall denote either a decimal fixed point subtype or a floating
point subtype (notwithstanding the rule given in 3.5.9 that only allows a
decimal fixed point subtype).

        6.a   Discussion:  We may need a better way to deal with obsolescent
        features with rules that contradict those of the non-obsolescent
        parts of the standard.


                              Static Semantics

7   A subtype_indication with a subtype_mark that denotes an ordinary fixed
point subtype and a delta_constraint defines an ordinary fixed point subtype
with a delta given by the value of the expression of the delta_constraint.
{94-4774.f} If the delta_constraint includes a range_constraint, then the
ordinary fixed point subtype is constrained by the range_constraint.

8   A subtype_indication with a subtype_mark that denotes a floating point
subtype and a digits_constraint defines a floating point subtype with a
requested decimal precision (as reflected by its Digits attribute) given by
the value of the expression of the digits_constraint.  If the digits_
constraint includes a range_constraint, then the floating point subtype is
constrained by the range_constraint.


                              Dynamic Semantics

9   {compatibility [delta_constraint with an ordinary fixed point subtype]} A
delta_constraint is compatible with an ordinary fixed point subtype if the
value of the expression is no less than the delta of the subtype, and the
range_constraint, if any, is compatible with the subtype.

10   {compatibility [digits_constraint with a floating point subtype]} A
digits_constraint is compatible with a floating point subtype if the value of
the expression is no greater than the requested decimal precision of the
subtype, and the range_constraint, if any, is compatible with the subtype.

11   {elaboration [delta_constraint]} The elaboration of a delta_constraint
consists of the elaboration of the range_constraint, if any.

        11.a   Reason:  A numeric subtype is considered ``constrained'' only
        if a range constraint applies to it.  The only effect of a digits_
        constraint or a delta_constraint without a range_constraint is to
        specify the value of the corresponding Digits or Delta attribute in
        the new subtype.  The set of values of the subtype is not
        ``constrained'' in any way by such _constraints.


                         Wording Changes From Ada 83

        11.b   In Ada 83, a delta_constraint is called a fixed_point_
        constraint, and a digits_constraint is called a floating_point_
        constraint.  We have adopted other terms because digits_constraints
        apply primarily to decimal fixed point types now (they apply to
        floating point types only as an obsolescent feature).



J.4 The Constrained Attribute

                              Static Semantics

1   For every private subtype S,

        1.a   Discussion:  including a generic formal private subtype

the following attribute is defined:

2   S'Constrained
                Yields the value False if S denotes an unconstrained
                nonformal private subtype with discriminants; also yields the
                value False if S denotes a generic formal private subtype,
                and the associated actual subtype is either an unconstrained
                subtype with discriminants or an unconstrained array subtype;
                yields the value True otherwise.  The value of this attribute
                is of the predefined subtype Boolean.

2.a     Reason:  Because Ada 9X has unknown_discriminant_parts, the
        Constrained attribute of private subtypes is obsolete.  This is
        fortunate, since its Ada 83 definition was confusing, as explained
        below.  Because this attribute is obsolete, we do not bother to
        extend its definition to private extensions.

2.b     The Constrained attribute of an object is not obsolete.

2.c     Note well: S'Constrained matches the Ada 9X definition of
        ``constrained'' only for composite subtypes.  For elementary
        subtypes, S'Constrained is always true, whether or not S is
        constrained.  (The Constrained attribute of an object does not have
        this problem, as it is only defined for objects of a discriminated
        type.)  So one should think of its designator as being
        'Constrained_Or_Elementary.



J.5 ASCII

                              Static Semantics

1   The following declaration exists in the declaration of package Standard:

2      package ASCII is

3         --  Control characters:

4
          NUL   : constant Character := nul;     SOH   : constant Character := \
soh;
          STX   : constant Character := stx;     ETX   : constant Character := \
etx;
          EOT   : constant Character := eot;     ENQ   : constant Character := \
enq;
          ACK   : constant Character := ack;     BEL   : constant Character := \
bel;
          BS    : constant Character := bs;      HT    : constant Character := \
ht;
          LF    : constant Character := lf;      VT    : constant Character := \
vt;
          FF    : constant Character := ff;      CR    : constant Character := \
cr;
          SO    : constant Character := so;      SI    : constant Character := \
si;
          DLE   : constant Character := dle;     DC1   : constant Character := \
dc1;
          DC2   : constant Character := dc2;     DC3   : constant Character := \
dc3;
          DC4   : constant Character := dc4;     NAK   : constant Character := \
nak;
          SYN   : constant Character := syn;     ETB   : constant Character := \
etb;
          CAN   : constant Character := can;     EM    : constant Character := \
em;
          SUB   : constant Character := sub;     ESC   : constant Character := \
esc;
          FS    : constant Character := fs;      GS    : constant Character := \
gs;
          RS    : constant Character := rs;      US    : constant Character := \
us;
          DEL   : constant Character := del;

5         -- Other characters:

6         Exclam    : constant Character:= '!';  Quotation : constant Character\
:= '"';
          Sharp     : constant Character:= '#';  Dollar    : constant Character\
:= '$';
          Percent   : constant Character:= '%';  Ampersand : constant Character\
:= '&';
          Colon     : constant Character:= ':';  Semicolon : constant Character\
:= ';';
          Query     : constant Character:= '?';  At_Sign   : constant Character\
:= '@';
          L_Bracket : constant Character:= '[';  Back_Slash: constant Character\
:= '\';
          R_Bracket : constant Character:= ']';  Circumflex: constant Character\
:= '^';
          Underline : constant Character:= '_';  Grave     : constant Character\
:= '`';
          L_Brace   : constant Character:= '{';  Bar       : constant Character\
:= '|';
          R_Brace   : constant Character:= '}';  Tilde     : constant Character\
:= '~';

7         -- Lower case letters:

8         LC_A: constant Character:= 'a';
          ...
          LC_Z: constant Character:= 'z';

9      end ASCII;

{94-4977.a}



J.6 Numeric_Error

                              Static Semantics

1   The following declaration exists in the declaration of package Standard:

2   Numeric_Error : exception renames Constraint_Error;

        2.a   Discussion:  This is true even though it is not shown in A.1.

        2.b   Reason:  In Ada 83, it was unclear which situations should
        raise Numeric_Error, and which should raise Constraint_Error.  The
        permissions of RM83-11.6 could often be used to allow the
        implementation to raise Constraint_Error in a situation where one
        would normally expect Numeric_Error.  To avoid this confusion, all
        situations that raise Numeric_Error in Ada 83 are changed to raise
        Constraint_Error in Ada 9X.  Numeric_Error is changed to be a
        renaming of Constraint_Error to avoid most of the upward
        compatibilities associated with this change.

        2.c   In new code, Constraint_Error should be used instead of
        Numeric_Error.



J.7 At Clauses

                                   Syntax

1   at_clause ::= for direct_name use at expression;


                              Static Semantics

2   An at_clause of the form ``for x use at y;'' is equivalent to an
attribute_definition_clause of the form ``for x'Address use y;''.

        2.a   Reason:  The preferred syntax for specifying the address of an
        entity is an attribute_definition_clause specifying the Address
        attribute.  Therefore, the special-purpose at_clause syntax is now
        obsolete.

        2.b   The above equivalence implies, for example, that only one at_
        clause is allowed for a given entity.  Similarly, it is illegal to
        give both an at_clause and an attribute_definition_clause specifying
        the Address attribute.


                            Extensions to Ada 83

        2.c   {extensions to Ada 83} We now allow to define the address of an
        entity using an attribute_definition_clause.  This is because Ada
        83's at_clause is so hard to remember: programmers often tend to
        write ``for X'Address use...;''.

                         Wording Changes From Ada 83

        2.d   Ada 83's address_clause is now called an at_clause to avoid
        confusion with the new term ``Address clause'' (that is, an
        attribute_definition_clause for the Address attribute).



J.7.1 Interrupt Entries

1   [Implementations are permitted to allow the attachment of task entries to
interrupts via the address clause.  Such an entry is referred to as an
interrupt entry.

2   The address of the task entry corresponds to a hardware interrupt in an
implementation-defined manner.  (See Ada.Interrupts.Reference in C.3.2.)]


                              Static Semantics

3   The following attribute is defined:

4   For any task entry X:

5   {interrupt entry} X'Address
                For a task entry whose address is specified (an interrupt
                entry), the value refers to the corresponding hardware
                interrupt.  For such an entry, as for any other task entry,
                the meaning of this value is implementation defined.  The
                value of this attribute is of the type of the subtype
                System.Address.

                6   {specifiable [of Address for entries]} Address may be
                specified for single entries via an attribute_definition_
                clause.

6.a     Reason:  Because of the equivalence of at_clauses and attribute_
        definition_clauses, an interrupt entry may be specified via either
        notation.


                              Dynamic Semantics

7   {initialization [of a task object]} As part of the initialization of a
task object, the address clause for an interrupt entry is elaborated[, which
evaluates the expression of the address clause].  A check is made that the
address specified is associated with some interrupt to which a task entry may
be attached.  {Program_Error (raised by failure of run-time check)} If this
check fails, Program_Error is raised.  Otherwise, the interrupt entry is
attached to the interrupt associated with the specified address.

8   {finalization [of a task object]} Upon finalization of the task object,
the interrupt entry, if any, is detached from the corresponding interrupt and
the default treatment is restored.

9   While an interrupt entry is attached to an interrupt, the interrupt is
reserved (see C.3).

10   An interrupt delivered to a task entry acts as a call to the entry
issued by a hardware task whose priority is in the System.Interrupt_Priority
range.  It is implementation defined whether the call is performed as an
ordinary entry call, a timed entry call, or a conditional entry call; which
kind of call is performed can depend on the specific interrupt.


                          Bounded (Run-Time) Errors

11   {bounded error} It is a bounded error to evaluate E'Caller (see C.7.1)
in an accept_statement for an interrupt entry.  The possible effects are the
same as for calling Current_Task from an entry body.


                         Documentation Requirements

12   {documentation requirements} The implementation shall document to which
interrupts a task entry may be attached.

13   The implementation shall document whether the invocation of an interrupt
entry has the effect of an ordinary entry call, conditional call, or a timed
call, and whether the effect varies in the presence of pending interrupts.


                         Implementation Permissions

14   The support for this subclause is optional.

15   Interrupts to which the implementation allows a task entry to be
attached may be designated as reserved for the entire duration of program
execution[; that is, not just when they have an interrupt entry attached to
them].

16   Interrupt entry calls may be implemented by having the hardware execute
directly the appropriate accept body.  Alternatively, the implementation is
allowed to provide an internal interrupt handler to simulate the effect of a
normal task calling the entry.

17   The implementation is allowed to impose restrictions on the
specifications and bodies of tasks that have interrupt entries.

18   It is implementation defined whether direct calls (from the program) to
interrupt entries are allowed.

19   If a select_statement contains both a terminate_alternative and an
accept_alternative for an interrupt entry, then an implementation is allowed
to impose further requirements for the selection of the terminate_alternative
in addition to those given in 9.3.


     NOTES
20   (1) Queued interrupts correspond to ordinary entry calls.  Interrupts
     that are lost if not immediately processed correspond to conditional
     entry calls.  It is a consequence of the priority rules that an accept
     body executed in response to an interrupt can be executed with the
     active priority at which the hardware generates the interrupt, taking
     precedence over lower priority tasks, without a scheduling action.

21   (2) Control information that is supplied upon an interrupt can be passed
     to an associated interrupt entry as one or more parameters of mode in.


                                  Examples

22   Example of an interrupt entry:

23  task Interrupt_Handler is
      entry Done;
      for Done'Address use Ada.Interrupts.Reference(Ada.Interrupts.Names.Device\
_Done);
    end Interrupt_Handler;

{94-4761.zb} {94-4765.a} {94-4846.d}


                         Wording Changes From Ada 83

        23.a   RM83-13.5.1 did not adequately address the problems associate
        with interrupts.  This feature is now obsolescent and is replaced by
        the Ada 9X interrupt model as specified in the Systems Programming
        Annex.



J.8 Mod Clauses

                                   Syntax

1   mod_clause ::= at mod static_expression;


                              Static Semantics

2   A record_representation_clause of the form:

3   for r use
        record at mod a
            ...
        end record;

4   is equivalent to:

5   for r'Alignment use a;
    for r use
        record
            ...
        end record;

        5.a   Reason:  The preferred syntax for specifying the alignment of
        an entity is an attribute_definition_clause specifying the Alignment
        attribute.  Therefore, the special-purpose mod_clause syntax is now
        obsolete.

        5.b   The above equivalence implies, for example, that it is illegal
        to give both a mod_clause and an attribute_definition_clause
        specifying the Alignment attribute for the same type.


                         Wording Changes From Ada 83

        5.c   Ada 83's alignment_clause is now called a mod_clause to avoid
        confusion with the new term ``Alignment clause'' (that is, an
        attribute_definition_clause for the Alignment attribute).



J.9 The Storage_Size Attribute

                              Static Semantics

1   For any task subtype T, the following attribute is defined:

2   T'Storage_Size
                Denotes an implementation-defined value of type universal_
                integer representing the number of storage elements reserved
                for a task of the subtype T.

        2.a   To be honest:  T'Storage_Size cannot be particularly meaningful
        in the presence of a pragma Storage_Size, especially when the
        expression is dynamic, or depends on a discriminant of the task,
        because the Storage_Size will be different for different objects of
        the type.  Even without such a pragma, the Storage_Size can be
        different for different objects of the type, and in any case, the
        value is implementation defined.  Hence, it is always implementation
        defined.

                3   {specifiable [of Storage_Size for a task first subtype]}
                Storage_Size may be specified for a task first subtype via an
                attribute_definition_clause.



                                   Annex K
                                (informative)


                         Language-Defined Attributes



1   {attribute} This annex summarizes the definitions given elsewhere of the
language-defined attributes.  {94-4693.o}

2   P'Access
                For a prefix P that denotes a subprogram:

                3   P'Access yields an access value that designates the
                subprogram denoted by P. The type of P'Access is an
                access-to-subprogram type (S), as determined by the expected
                type.  See 3.10.2.

4   X'Access
                For a prefix X that denotes an aliased view of an object:

                5   X'Access yields an access value that designates the
                object denoted by X. The type of X'Access is an
                access-to-object type, as determined by the expected type.
                The expected type shall be a general access type.  See
                3.10.2.

6   X'Address
                For a prefix X that denotes an object, program unit, or
                label:

                7   Denotes the address of the first of the storage elements
                allocated to X. For a program unit or label, this value
                refers to the machine code associated with the corresponding
                body or statement.  The value of this attribute is of type
                System.Address.  See 13.3.

8   S'Adjacent
                For every subtype S of a floating point type T:

                9   S'Adjacent denotes a function with the following
                specification:

10                  function S'Adjacent (X, Towards : T)
                      return T

                11   {Constraint_Error (raised by failure of run-time check)}
                If Towards=X, the function yields X; otherwise, it yields the
                machine number of the type T adjacent to X in the direction
                of Towards, if that machine number exists.  {Range_Check
                [partial]} {check, language-defined (Range_Check)} If the
                result would be outside the base range of S, Constraint_Error
                is raised.  When T'Signed_Zeros is True, a zero result has
                the sign of X.  When Towards is zero, its sign has no bearing
                on the result.  See A.5.3.

12  S'Aft
                For every fixed point subtype S:

                13   S'Aft yields the number of decimal digits needed after
                the decimal point to accommodate the delta of the subtype S,
                unless the delta of the subtype S is greater than 0.1, in
                which case the attribute yields the value one.  [(S'Aft is
                the smallest positive integer N for which (10**N)*S'Delta is
                greater than or equal to one.)]  The value of this attribute
                is of the type universal_integer.  See 3.5.10.

14  X'Alignment
                For a prefix X that denotes a subtype or object:

                15   The Address of an object that is allocated under control
                of the implementation is an integral multiple of the
                Alignment of the object (that is, the Address modulo the
                Alignment is zero).  The offset of a record component is a
                multiple of the Alignment of the component.  For an object
                that is not allocated under control of the implementation
                (that is, one that is imported, that is allocated by a
                user-defined allocator, whose Address has been specified, or
                is designated by an access value returned by an instance of
                Unchecked_Conversion), the implementation may assume that the
                Address is an integral multiple of its Alignment.  The
                implementation shall not assume a stricter alignment.

                16   The value of this attribute is of type universal_
                integer, and nonnegative; zero means that the object is not
                necessarily aligned on a storage element boundary.  See 13.3.

17  S'Base
                For every scalar subtype S:

                18   S'Base denotes an unconstrained subtype of the type of
                S. This unconstrained subtype is called the base subtype of
                the type.  See 3.5.

19  S'Bit_Order
                For every specific record subtype S:

                20   Denotes the bit ordering for the type of S. The value of
                this attribute is of type System.Bit_Order.  See 13.5.3.

21  P'Body_Version
                For a prefix P that statically denotes a program unit:

                22   Yields a value of the predefined type String that
                identifies the version of the compilation unit that contains
                the body (but not any subunits) of the program unit.  See
                E.3.

23  T'Callable
                For a prefix T that is of a task type [(after any implicit
                dereference)]:

                24   Yields the value True when the task denoted by T is
                callable, and False otherwise; See 9.9.

25  E'Caller
                For a prefix E that denotes an entry_declaration:

                26   Yields a value of the type Task_ID that identifies the
                task whose call is now being serviced.  Use of this attribute
                is allowed only inside an entry_body or accept_statement
                corresponding to the entry_declaration denoted by E. See
                C.7.1.

27  S'Ceiling
                For every subtype S of a floating point type T:

                28   S'Ceiling denotes a function with the following
                specification:

29                  function S'Ceiling (X : T)
                      return T

                30   The function yields the value Ceiling(X), i.e., the
                smallest (most negative) integral value greater than or equal
                to X.  When X is zero, the result has the sign of X; a zero
                result otherwise has a negative sign when S'Signed_Zeros is
                True.  See A.5.3.

31  S'Class
                For every subtype S of a tagged type T (specific or
                class-wide):

                32   S'Class denotes a subtype of the class-wide type (called
                T'Class in this International Standard) for the class rooted
                at T (or if S already denotes a class-wide subtype, then
                S'Class is the same as S).

                33   {unconstrained (subtype)} {constrained (subtype)}
                S'Class is unconstrained.  However, if S is constrained, then
                the values of S'Class are only those that when converted to
                the type T belong to S. See 3.9.

34  S'Class
                For every subtype S of an untagged private type whose full
                view is tagged:

                35   Denotes the class-wide subtype corresponding to the full
                view of S. This attribute is allowed only from the beginning
                of the private part in which the full view is declared, until
                the declaration of the full view.  [After the full view, the
                Class attribute of the full view can be used.]  See 7.3.1.

36  X'Component_Size
                For a prefix X that denotes an array subtype or array object
                [(after any implicit dereference)]:

                37   Denotes the size in bits of components of the type of
                X. The value of this attribute is of type universal_integer.
                See 13.3.

38  S'Compose
                For every subtype S of a floating point type T:

                39   S'Compose denotes a function with the following
                specification:

40                  function S'Compose (Fraction : T;
                                        Exponent : universal_integer)
                      return T

                41   {Constraint_Error (raised by failure of run-time check)}
                                                           Exponent-k
                Let v be the value Fraction*T'Machine_Radix          , where
                k is the normalized exponent of Fraction.  If v is a machine
                number of the type T, or if |v|>=T'Model_Small, the function
                yields v; otherwise, it yields either one of the machine
                numbers of the type T adjacent to v.  {Range_Check [partial]}
                {check, language-defined (Range_Check)} Constraint_Error is
                optionally raised if v is outside the base range of S. A zero
                result has the sign of Fraction when S'Signed_Zeros is True.
                See A.5.3.

42  A'Constrained
                For a prefix A that is of a discriminated type [(after any
                implicit dereference)]:

                43   Yields the value True if A denotes a constant, a value,
                or a constrained variable, and False otherwise.  See 3.7.2.

44  S'Copy_Sign
                For every subtype S of a floating point type T:

                45   S'Copy_Sign denotes a function with the following
                specification:

46                  function S'Copy_Sign (Value, Sign : T)
                      return T

                47   {Constraint_Error (raised by failure of run-time check)}
                If the value of Value is nonzero, the function yields a
                result whose magnitude is that of Value and whose sign is
                that of Sign; otherwise, it yields the value zero.  {Range_
                Check [partial]} {check, language-defined (Range_Check)}
                Constraint_Error is optionally raised if the result is
                outside the base range of S. A zero result has the sign of
                Sign when S'Signed_Zeros is True.  See A.5.3.

48  E'Count
                For a prefix E that denotes an entry of a task or protected
                unit:

                49   Yields the number of calls presently queued on the entry
                E of the current instance of the unit.  The value of this
                attribute is of the type universal_integer.  See 9.9.

50  S'Definite
                For a prefix S that denotes a formal indefinite subtype:

                51   S'Definite yields True if the actual subtype
                corresponding to S is definite; otherwise it yields False.
                The value of this attribute is of the predefined type
                Boolean.  See 12.5.1.

52  S'Delta
                For every fixed point subtype S:

                53   S'Delta denotes the delta of the fixed point subtype
                S. The value of this attribute is of the type universal_real.
                See 3.5.10.

54  S'Denorm
                For every subtype S of a floating point type T:

                55   Yields the value True if every value expressible in the
                form

                                               T'Machine_Emin
                    +/-mantissa*T'Machine_Radix

                where mantissa is a nonzero T'Machine_Mantissa-digit fraction
                in the number base T'Machine_Radix, the first digit of which
                is zero, is a machine number (see 3.5.7) of the type T;
                yields the value False otherwise.  The value of this
                attribute is of the predefined type Boolean.  See A.5.3.

56  S'Digits
                For every decimal fixed point subtype S:

                57   S'Digits denotes the digits of the decimal fixed point
                subtype S, which corresponds to the number of decimal digits
                that are representable in objects of the subtype.  The value
                of this attribute is of the type universal_integer.  See
                3.5.10.

58  S'Digits
                For every floating point subtype S:

                59   S'Digits denotes the requested decimal precision for the
                subtype S. The value of this attribute is of the type
                universal_integer.  See 3.5.8.

60  S'Exponent
                For every subtype S of a floating point type T:

                61   S'Exponent denotes a function with the following
                specification:

62                  function S'Exponent (X : T)
                      return universal_integer

                63   The function yields the normalized exponent of X.  See
                A.5.3.

64  S'External_Tag
                For every subtype S of a tagged type T (specific or
                class-wide):

                65   {External_Tag clause} {specifiable [of External_Tag for
                a tagged type]} S'External_Tag denotes an external string
                representation for S'Tag; it is of the predefined type
                String.  External_Tag may be specified for a specific tagged
                type via an attribute_definition_clause; the expression of
                such a clause shall be static.  The default external tag
                representation is implementation defined.  See 3.9.2 and
                13.13.2.  See 13.3.

66  A'First(N)
                For a prefix A that is of an array type [(after any implicit
                dereference)], or denotes a constrained array subtype:

                67   A'First(N) denotes the lower bound of the N-th index
                range; its type is the corresponding index type.  See 3.6.2.

68  A'First
                For a prefix A that is of an array type [(after any implicit
                dereference)], or denotes a constrained array subtype:

                69   A'First denotes the lower bound of the first index
                range; its type is the corresponding index type.  See 3.6.2.

70  S'First
                For every scalar subtype S:

                71   S'First denotes the lower bound of the range of S. The
                value of this attribute is of the type of S. See 3.5.

72  R.C'First_Bit
                For a component C of a composite, non-array object R:

                73   Denotes the offset, from the start of the first of the
                storage elements occupied by C, of the first bit occupied by
                C. This offset is measured in bits.  The first bit of a
                storage element is numbered zero.  The value of this
                attribute is of the type universal_integer.  See 13.5.2.

74  S'Floor
                For every subtype S of a floating point type T:

                75   S'Floor denotes a function with the following
                specification:

76                  function S'Floor (X : T)
                      return T

                77   The function yields the value Floor(X), i.e., the
                largest (most positive) integral value less than or equal to
                X.  When X is zero, the result has the sign of X; a zero
                result otherwise has a positive sign.  See A.5.3.

78  S'Fore
                For every fixed point subtype S:

                79   S'Fore yields the minimum number of characters needed
                before the decimal point for the decimal representation of
                any value of the subtype S, assuming that the representation
                does not include an exponent, but includes a one-character
                prefix that is either a minus sign or a space.  (This minimum
                number does not include superfluous zeros or underlines, and
                is at least 2.)  The value of this attribute is of the type
                universal_integer.  See 3.5.10.

80  S'Fraction
                For every subtype S of a floating point type T:

                81   S'Fraction denotes a function with the following
                specification:

82                  function S'Fraction (X : T)
                      return T

                                                                    -k
                83   The function yields the value X*T'Machine_Radix  , where
                k is the normalized exponent of X.  A zero result[, which can
                only occur when X is zero,] has the sign of X.  See A.5.3.

84  E'Identity
                For a prefix E that denotes an exception:

                85   E'Identity returns the unique identity of the exception.
                The type of this attribute is Exception_Id.  See 11.4.1.

86  T'Identity
                For a prefix T that is of a task type [(after any implicit
                dereference)]:

                87   Yields a value of the type Task_ID that identifies the
                task denoted by T. See C.7.1.

88  S'Image
                For every scalar subtype S:

                89   S'Image denotes a function with the following
                specification:

90                  function S'Image(Arg : S'Base)
                      return String

                91   The function returns an image of the value of Arg as a
                String.  See 3.5.

92  S'Class'Input
                For every subtype S'Class of a class-wide type T'Class:

                93   S'Class'Input denotes a function with the following
                specification:

94                  function S'Class'Input(
                       Stream : access Ada.Streams.Root_Stream_Type'Class)
                       return T'Class

                {94-4768.u}

                95   First reads the external tag from Stream and determines
                the corresponding internal tag (by calling Tags.Internal_
                Tag(String'Input(Stream)) -- see 3.9) and then dispatches to
                the subprogram denoted by the Input attribute of the specific
                type identified by the internal tag; returns that result.
                See 13.13.2.

96  S'Input
                For every subtype S of a specific type T:

                97   S'Input denotes a function with the following
                specification:

98                  function S'Input(
                       Stream : access Ada.Streams.Root_Stream_Type'Class)
                       return T

                99   S'Input reads and returns one value from Stream, using
                any bounds or discriminants written by a corresponding
                S'Output to determine how much to read.  See 13.13.2.

100 A'Last(N)
                For a prefix A that is of an array type [(after any implicit
                dereference)], or denotes a constrained array subtype:

                101   A'Last(N) denotes the upper bound of the N-th index
                range; its type is the corresponding index type.  See 3.6.2.

102 A'Last
                For a prefix A that is of an array type [(after any implicit
                dereference)], or denotes a constrained array subtype:

                103   A'Last denotes the upper bound of the first index
                range; its type is the corresponding index type.  See 3.6.2.

104 S'Last
                For every scalar subtype S:

                105   S'Last denotes the upper bound of the range of S. The
                value of this attribute is of the type of S. See 3.5.

106 R.C'Last_Bit
                For a component C of a composite, non-array object R:

                107   Denotes the offset, from the start of the first of the
                storage elements occupied by C, of the last bit occupied by
                C. This offset is measured in bits. The value of this
                attribute is of the type universal_integer.  See 13.5.2.

108 S'Leading_Part
                For every subtype S of a floating point type T:

                109   S'Leading_Part denotes a function with the following
                specification:

110                 function S'Leading_Part (X : T;
                                             Radix_Digits : universal_integer)
                      return T

                                                        k-Radix_Digits
                111   Let v be the value T'Machine_Radix              , where
                k is the normalized exponent of X.  The function yields the
                value

                  112  Floor(X/v)*v, when X is nonnegative and Radix_
                       Digits is positive;

                  113  Ceiling(X/v)*v, when X is negative and Radix_
                       Digits is positive.

                114   {Constraint_Error (raised by failure of run-time
                check)} {Range_Check [partial]} {check, language-defined
                (Range_Check)} Constraint_Error is raised when Radix_Digits
                is zero or negative.  A zero result[, which can only occur
                when X is zero,] has the sign of X.  See A.5.3.

115 A'Length(N)
                For a prefix A that is of an array type [(after any implicit
                dereference)], or denotes a constrained array subtype:

                116   A'Length(N) denotes the number of values of the N-th
                index range (zero for a null range); its type is universal_
                integer.  See 3.6.2.

117 A'Length
                For a prefix A that is of an array type [(after any implicit
                dereference)], or denotes a constrained array subtype:

                118   A'Length denotes the number of values of the first
                index range (zero for a null range); its type is universal_
                integer.  See 3.6.2.

119 S'Machine
                For every subtype S of a floating point type T:

                120   S'Machine denotes a function with the following
                specification:

121                 function S'Machine (X : T)
                      return T

                122   {Constraint_Error (raised by failure of run-time
                check)} If X is a machine number of the type T, the function
                yields X; otherwise, it yields the value obtained by rounding
                or truncating X to either one of the adjacent machine numbers
                of the type T.  {Range_Check [partial]} {check,
                language-defined (Range_Check)} Constraint_Error is raised if
                rounding or truncating X to the precision of the machine
                numbers results in a value outside the base range of S. A
                zero result has the sign of X when S'Signed_Zeros is True.
                See A.5.3.

123 S'Machine_Emax
                For every subtype S of a floating point type T:

                124   Yields the largest (most positive) value of exponent
                such that every value expressible in the canonical form (for
                the type T), having a mantissa of T'Machine_Mantissa digits,
                is a machine number (see 3.5.7) of the type T.  This
                attribute yields a value of the type universal_integer.  See
                A.5.3.

125 S'Machine_Emin
                For every subtype S of a floating point type T:

                126   Yields the smallest (most negative) value of exponent
                such that every value expressible in the canonical form (for
                the type T), having a mantissa of T'Machine_Mantissa digits,
                is a machine number (see 3.5.7) of the type T.  This
                attribute yields a value of the type universal_integer.  See
                A.5.3.

127 S'Machine_Mantissa
                For every subtype S of a floating point type T:

                128   Yields the largest value of p such that every value
                expressible in the canonical form (for the type T), having a
                p-digit mantissa and an exponent between T'Machine_Emin and
                T'Machine_Emax, is a machine number (see 3.5.7) of the type
                T.  This attribute yields a value of the type universal_
                integer.  See A.5.3.

129 S'Machine_Overflows
                For every subtype S of a fixed point type T:

                130   Yields the value True if overflow and divide-by-zero
                are detected and reported by raising Constraint_Error for
                every predefined operation that yields a result of the type
                T; yields the value False otherwise.  The value of this
                attribute is of the predefined type Boolean.  See A.5.4.

131 S'Machine_Overflows
                For every subtype S of a floating point type T:

                132   Yields the value True if overflow and divide-by-zero
                are detected and reported by raising Constraint_Error for
                every predefined operation that yields a result of the type
                T; yields the value False otherwise.  The value of this
                attribute is of the predefined type Boolean.  See A.5.3.

133 S'Machine_Radix
                For every subtype S of a fixed point type T:

                134   Yields the radix of the hardware representation of the
                type T.  The value of this attribute is of the type
                universal_integer.  See A.5.4.

135 S'Machine_Radix
                For every subtype S of a floating point type T:

                136   Yields the radix of the hardware representation of the
                type T.  The value of this attribute is of the type
                universal_integer.  See A.5.3.

137 S'Machine_Rounds
                For every subtype S of a fixed point type T:

                138   Yields the value True if rounding is performed on
                inexact results of every predefined operation that yields a
                result of the type T; yields the value False otherwise.  The
                value of this attribute is of the predefined type Boolean.
                See A.5.4.

139 S'Machine_Rounds
                For every subtype S of a floating point type T:

                140   Yields the value True if rounding is performed on
                inexact results of every predefined operation that yields a
                result of the type T; yields the value False otherwise.  The
                value of this attribute is of the predefined type Boolean.
                See A.5.3.

141 S'Max
                For every scalar subtype S:

                142   S'Max denotes a function with the following
                specification:

143                 function S'Max(Left, Right : S'Base)
                      return S'Base

                144   The function returns the greater of the values of the
                two parameters.  See 3.5.

145 S'Max_Size_In_Storage_Elements
                For every subtype S:

                146   Denotes the maximum value for Size_In_Storage_Elements
                that will be requested via Allocate for an access type whose
                designated subtype is S. The value of this attribute is of
                type universal_integer.  See 13.11.1.

147 S'Min
                For every scalar subtype S:

                148   S'Min denotes a function with the following
                specification:

149                 function S'Min(Left, Right : S'Base)
                      return S'Base

                150   The function returns the lesser of the values of the
                two parameters.  See 3.5.

151 S'Model
                For every subtype S of a floating point type T:

                152   S'Model denotes a function with the following
                specification:

153                 function S'Model (X : T)
                      return T

                154   If the Numerics Annex is not supported, the meaning of
                this attribute is implementation defined; see G.2.2 for the
                definition that applies to implementations supporting the
                Numerics Annex.  See A.5.3.

155 S'Model_Emin
                For every subtype S of a floating point type T:

                156   If the Numerics Annex is not supported, this attribute
                yields an implementation defined value that is greater than
                or equal to the value of T'Machine_Emin.  See G.2.2 for
                further requirements that apply to implementations supporting
                the Numerics Annex.  The value of this attribute is of the
                type universal_integer.  See A.5.3.

157 S'Model_Epsilon
                For every subtype S of a floating point type T:
                                                      1-T'Model_Mantissa
                158   Yields the value T'Machine_Radix                  .
                The value of this attribute is of the type universal_real.
                See A.5.3.

159 S'Model_Mantissa
                For every subtype S of a floating point type T:

                160   If the Numerics Annex is not supported, this attribute
                yields an implementation defined value that is greater than
                or equal to Ceiling(d*log (10)/log (T'Machine_Radix))+1,
                where d is the requested decimal precision of T, and less
                than or equal to the value of T'Machine_Mantissa.  See G.2.2
                for further requirements that apply to implementations
                supporting the Numerics Annex.  The value of this attribute
                is of the type universal_integer.  See A.5.3.

161 S'Model_Small
                For every subtype S of a floating point type T:
                                                      T'Model_Emin-1
                162   Yields the value T'Machine_Radix              .  The
                value of this attribute is of the type universal_real.  See
                A.5.3.

163 S'Modulus
                For every modular subtype S:

                164   S'Modulus yields the modulus of the type of S, as a
                value of the type universal_integer.  See 3.5.4.

165 S'Class'Output
                For every subtype S'Class of a class-wide type T'Class:

                166   S'Class'Output denotes a procedure with the following
                specification:

167                 procedure S'Class'Output(
                       Stream : access Ada.Streams.Root_Stream_Type'Class;
                       Item   : in T'Class)

                168   First writes the external tag of Item to Stream (by
                calling String'Output(Tags.External_Tag(Item'Tag) -- see 3.9)
                and then dispatches to the subprogram denoted by the Output
                attribute of the specific type identified by the tag.  See
                13.13.2.

169 S'Output
                For every subtype S of a specific type T:

                170   S'Output denotes a procedure with the following
                specification:

171                 procedure S'Output(
                       Stream : access Ada.Streams.Root_Stream_Type'Class;
                       Item : in T)

                172   S'Output writes the value of Item to Stream, including
                any bounds or discriminants.  See 13.13.2.

173 D'Partition_ID
                For a prefix D that denotes a library-level declaration,
                excepting a declaration of or within a declared-pure library
                unit:

                174   Denotes a value of the type universal_integer that
                identifies the partition in which D was elaborated.  If D
                denotes the declaration of a remote call interface library
                unit (see E.2.3) the given partition is the one where the
                body of D was elaborated.  See E.1.

175 S'Pos
                For every discrete subtype S:

                176   S'Pos denotes a function with the following
                specification:

177                 function S'Pos(Arg : S'Base)
                      return universal_integer

                178   This function returns the position number of the value
                of Arg, as a value of type universal_integer.  See 3.5.5.

179 R.C'Position
                For a component C of a composite, non-array object R:

                180   Denotes the same value as R.C'Address - R'Address.  The
                value of this attribute is of the type universal_integer.
                See 13.5.2.

181 S'Pred
                For every scalar subtype S:

                182   S'Pred denotes a function with the following
                specification:

183                 function S'Pred(Arg : S'Base)
                      return S'Base

                184   {Constraint_Error (raised by failure of run-time
                check)} For an enumeration type, the function returns the
                value whose position number is one less than that of the
                value of Arg; {Range_Check [partial]} {check,
                language-defined (Range_Check)} Constraint_Error is raised if
                there is no such value of the type.  For an integer type, the
                function returns the result of subtracting one from the value
                of Arg.  For a fixed point type, the function returns the
                result of subtracting small from the value of Arg.  For a
                floating point type, the function returns the machine number
                (as defined in 3.5.7) immediately below the value of Arg;
                {Range_Check [partial]} {check, language-defined (Range_
                Check)} Constraint_Error is raised if there is no such
                machine number.  See 3.5.

185 A'Range(N)
                For a prefix A that is of an array type [(after any implicit
                dereference)], or denotes a constrained array subtype:

                186   A'Range(N) is equivalent to the range A'First(N) ..
                A'Last(N), except that the prefix A is only evaluated once.
                See 3.6.2.

187 A'Range
                For a prefix A that is of an array type [(after any implicit
                dereference)], or denotes a constrained array subtype:

                188   A'Range is equivalent to the range A'First .. A'Last,
                except that the prefix A is only evaluated once.  See 3.6.2.

189 S'Range
                For every scalar subtype S:

                190   S'Range is equivalent to the range S'First .. S'Last.
                See 3.5.

191 S'Class'Read
                For every subtype S'Class of a class-wide type T'Class:

                192   S'Class'Read denotes a procedure with the following
                specification:

193                 procedure S'Class'Read(
                       Stream : access Ada.Streams.Root_Stream_Type'Class;
                       Item : out T'Class)

                194   Dispatches to the subprogram denoted by the Read
                attribute of the specific type identified by the tag of Item.
                See 13.13.2.

195 S'Read
                For every subtype S of a specific type T:

                196   S'Read denotes a procedure with the following
                specification:

197                 procedure S'Read(
                       Stream : access Ada.Streams.Root_Stream_Type'Class;
                       Item : out T)

                198   S'Read reads the value of Item from Stream.  See
                13.13.2.

199 S'Remainder
                For every subtype S of a floating point type T:

                200   S'Remainder denotes a function with the following
                specification:

201                 function S'Remainder (X, Y : T)
                      return T

                202   {Constraint_Error (raised by failure of run-time
                check)} For nonzero Y, let v be the value X-n*Y, where n is
                the integer nearest to the exact value of X/Y; if
                |n-X/Y|=1/2, then n is chosen to be even.  If v is a machine
                number of the type T, the function yields v; otherwise, it
                yields zero.  {Division_Check [partial]} {check,
                language-defined (Division_Check)} Constraint_Error is raised
                if Y is zero.  A zero result has the sign of X when S'Signed_
                Zeros is True.  See A.5.3.

203 S'Round
                For every decimal fixed point subtype S:

                204   S'Round denotes a function with the following
                specification:

205                 function S'Round(X : universal_real)
                      return S'Base

                206   The function returns the value obtained by rounding X
                (away from 0, if X is midway between two values of the type
                of S).  See 3.5.10.

207 S'Rounding
                For every subtype S of a floating point type T:

                208   S'Rounding denotes a function with the following
                specification:

209                 function S'Rounding (X : T)
                      return T

                210   The function yields the integral value nearest to X,
                rounding away from zero if X lies exactly halfway between two
                integers.  A zero result has the sign of X when S'Signed_
                Zeros is True.  See A.5.3.

211 S'Safe_First
                For every subtype S of a floating point type T:

                212   Yields the lower bound of the safe range (see 3.5.7) of
                the type T.  If the Numerics Annex is not supported, the
                value of this attribute is implementation defined; see G.2.2
                for the definition that applies to implementations supporting
                the Numerics Annex.  The value of this attribute is of the
                type universal_real.  See A.5.3.

213 S'Safe_Last
                For every subtype S of a floating point type T:

                214   Yields the upper bound of the safe range (see 3.5.7) of
                the type T.  If the Numerics Annex is not supported, the
                value of this attribute is implementation defined; see G.2.2
                for the definition that applies to implementations supporting
                the Numerics Annex.  The value of this attribute is of the
                type universal_real.  See A.5.3.

215 S'Scale
                For every decimal fixed point subtype S:

                216   S'Scale denotes the scale of the subtype S, defined as
                the value N such that S'Delta = 10.0**(-N).  {scale (of a
                decimal fixed point subtype)} [The scale indicates the
                position of the point relative to the rightmost significant
                digits of values of subtype S.]  The value of this attribute
                is of the type universal_integer.  See 3.5.10.

217 S'Scaling
                For every subtype S of a floating point type T:

                218   S'Scaling denotes a function with the following
                specification:

219                 function S'Scaling (X : T;
                                        Adjustment : universal_integer)
                      return T

                220   {Constraint_Error (raised by failure of run-time
                                                            Adjustment
                check)} Let v be the value X*T'Machine_Radix          .  If v
                is a machine number of the type T, or if |v|>=T'Model_Small,
                the function yields v; otherwise, it yields either one of the
                machine numbers of the type T adjacent to v.  {Range_Check
                [partial]} {check, language-defined (Range_Check)}
                Constraint_Error is optionally raised if v is outside the
                base range of S. A zero result has the sign of X when
                S'Signed_Zeros is True.  See A.5.3.

221 S'Signed_Zeros
                For every subtype S of a floating point type T:

                222   Yields the value True if the hardware representation
                for the type T has the capability of representing both
                positively and negatively signed zeros, these being generated
                and used by the predefined operations of the type T as
                specified in IEC 559:1989; yields the value False otherwise.
                The value of this attribute is of the predefined type
                Boolean.  See A.5.3.

223 S'Size
                For every subtype S:

                224   If S is definite, denotes the size [(in bits)] that the
                implementation would choose for the following objects of
                subtype S:

                  225  A record component of subtype S when the record
                       type is packed.

                  226  The formal parameter of an instance of Unchecked_
                       Conversion that converts from subtype S to some
                       other subtype.

                227   If S is indefinite, the meaning is implementation
                defined.  The value of this attribute is of the type
                universal_integer.  See 13.3.

228 X'Size
                For a prefix X that denotes an object:

                229   Denotes the size in bits of the representation of the
                object.  The value of this attribute is of the type
                universal_integer.  See 13.3.

230 S'Small
                For every fixed point subtype S:

                231   S'Small denotes the small of the type of S. The value
                of this attribute is of the type universal_real.  See 3.5.10.

232 S'Storage_Pool
                For every access subtype S:

                233   Denotes the storage pool of the type of S. The type of
                this attribute is Root_Storage_Pool'Class.  See 13.11.

234 S'Storage_Size
                For every access subtype S:

                235   Yields the result of calling Storage_Size(S'Storage_
                Pool)[, which is intended to be a measure of the number of
                storage elements reserved for the pool.]  The type of this
                attribute is universal_integer.  See 13.11.

236 T'Storage_Size
                For a prefix T that denotes a task object [(after any
                implicit dereference)]:

                237   Denotes the number of storage elements reserved for the
                task.  The value of this attribute is of the type universal_
                integer.  The Storage_Size includes the size of the task's
                stack, if any.  The language does not specify whether or not
                it includes other storage associated with the task (such as
                the ``task control block'' used by some implementations.)
                See 13.3.

238 S'Succ
                For every scalar subtype S:

                239   S'Succ denotes a function with the following
                specification:

240                 function S'Succ(Arg : S'Base)
                      return S'Base

                241   {Constraint_Error (raised by failure of run-time
                check)} For an enumeration type, the function returns the
                value whose position number is one more than that of the
                value of Arg; {Range_Check [partial]} {check,
                language-defined (Range_Check)} Constraint_Error is raised if
                there is no such value of the type.  For an integer type, the
                function returns the result of adding one to the value of
                Arg.  For a fixed point type, the function returns the result
                of adding small to the value of Arg.  For a floating point
                type, the function returns the machine number (as defined in
                3.5.7) immediately above the value of Arg; {Range_Check
                [partial]} {check, language-defined (Range_Check)}
                Constraint_Error is raised if there is no such machine
                number.  See 3.5.

242 S'Tag
                For every subtype S of a tagged type T (specific or
                class-wide):

                243   S'Tag denotes the tag of the type T (or if T is
                class-wide, the tag of the root type of the corresponding
                class).  The value of this attribute is of type Tag.  See
                3.9.

244 X'Tag
                For a prefix X that is of a class-wide tagged type [(after
                any implicit dereference)]:

                245   X'Tag denotes the tag of X. The value of this attribute
                is of type Tag.  See 3.9.

246 T'Terminated
                For a prefix T that is of a task type [(after any implicit
                dereference)]:

                247   Yields the value True if the task denoted by T is
                terminated, and False otherwise.  The value of this attribute
                is of the predefined type Boolean.  See 9.9.

248 S'Truncation
                For every subtype S of a floating point type T:

                249   S'Truncation denotes a function with the following
                specification:

250                 function S'Truncation (X : T)
                      return T

                251   The function yields the value Ceiling(X) when X is
                negative, and Floor(X) otherwise.  A zero result has the sign
                of X when S'Signed_Zeros is True.  See A.5.3.

252 S'Unbiased_Rounding
                For every subtype S of a floating point type T:

                253   S'Unbiased_Rounding denotes a function with the
                following specification:

254                 function S'Unbiased_Rounding (X : T)
                      return T

                255   The function yields the integral value nearest to X,
                rounding toward the even integer if X lies exactly halfway
                between two integers.  A zero result has the sign of X when
                S'Signed_Zeros is True.  See A.5.3.

256 X'Unchecked_Access
                For a prefix X that denotes an aliased view of an object:

                257   All rules and semantics that apply to X'Access (see
                3.10.2) apply also to X'Unchecked_Access, except that, for
                the purposes of accessibility rules and checks, it is as if X
                were declared immediately within a library package.  See
                13.10.

258 S'Val
                For every discrete subtype S:

                259   S'Val denotes a function with the following
                specification:

260                 function S'Val(Arg : universal_integer)
                      return S'Base

                261   {evaluation [Val]} {Constraint_Error (raised by failure
                of run-time check)} This function returns a value of the type
                of S whose position number equals the value of Arg.  See
                3.5.5.

262 X'Valid
                For a prefix X that denotes a scalar object [(after any
                implicit dereference)]:

                263   Yields True if and only if the object denoted by X is
                normal and has a valid representation.  The value of this
                attribute is of the predefined type Boolean.  See 13.9.2.

264 S'Value
                For every scalar subtype S:

                265   S'Value denotes a function with the following
                specification:

266                 function S'Value(Arg : String)
                      return S'Base

                267   This function returns a value given an image of the
                value as a String, ignoring any leading or trailing spaces.
                See 3.5.

268 P'Version
                For a prefix P that statically denotes a program unit:

                269   Yields a value of the predefined type String that
                identifies the version of the compilation unit that contains
                the declaration of the program unit.  See E.3.

270 S'Wide_Image
                For every scalar subtype S:

                271   S'Wide_Image denotes a function with the following
                specification:

272                 function S'Wide_Image(Arg : S'Base)
                      return Wide_String

                273   {image (of a value)} The function returns an image of
                the value of Arg, that is, a sequence of characters
                representing the value in display form.  See 3.5.

274 S'Wide_Value
                For every scalar subtype S:

                275   S'Wide_Value denotes a function with the following
                specification:

276                 function S'Wide_Value(Arg : Wide_String)
                      return S'Base

                277   This function returns a value given an image of the
                value as a Wide_String, ignoring any leading or trailing
                spaces.  See 3.5.

278 S'Wide_Width
                For every scalar subtype S:

                279   S'Wide_Width denotes the maximum length of a Wide_
                String returned by S'Wide_Image over all values of the
                subtype S. It denotes zero for a subtype that has a null
                range.  Its type is universal_integer.  See 3.5.

280 S'Width
                For every scalar subtype S:

                281   S'Width denotes the maximum length of a String returned
                by S'Image over all values of the subtype S. It denotes zero
                for a subtype that has a null range.  Its type is universal_
                integer.  See 3.5.

282 S'Class'Write
                For every subtype S'Class of a class-wide type T'Class:

                283   S'Class'Write denotes a procedure with the following
                specification:

284                 procedure S'Class'Write(
                       Stream : access Ada.Streams.Root_Stream_Type'Class;
                       Item   : in T'Class)

                285   Dispatches to the subprogram denoted by the Write
                attribute of the specific type identified by the tag of Item.
                See 13.13.2.

286 S'Write
                For every subtype S of a specific type T:

                287   S'Write denotes a procedure with the following
                specification:

288                 procedure S'Write(
                       Stream : access Ada.Streams.Root_Stream_Type'Class;
                       Item : in T)

                289   S'Write writes the value of Item to Stream.  See
                13.13.2.



                                   Annex L
                                (informative)


                           Language-Defined Pragmas



1   {pragma} This Annex summarizes the definitions given elsewhere of the
language-defined pragmas.  {94-4693.p}

2   pragma All_Calls_Remote[(library_unit_name)]; -- See E.2.3.

3   pragma Asynchronous(local_name); -- See E.4.1.

4   pragma Atomic(local_name); -- See C.6.

5   pragma Atomic_Components(array_local_name); -- See C.6.

6   pragma Attach_Handler(handler_name, expression); -- See C.3.1.

7   pragma Controlled(first_subtype_local_name); -- See 13.11.3.

8   pragma Convention([Convention =>] convention_identifier,[Entity =>]
local_name); -- See B.1.

9   pragma Discard_Names[([On => ] local_name)]; -- See C.5.

10   pragma Elaborate(library_unit_name{, library_unit_name}); -- See 10.2.1.

11   pragma Elaborate_All(library_unit_name{, library_unit_name}); -- See
10.2.1.

12   pragma Elaborate_Body[(library_unit_name)]; -- See 10.2.1.

13   pragma Export( [Convention =>] convention_identifier, [Entity =>] local_
name [, [External_Name =>] string_expression] [, [Link_Name =>]
string_expression]); -- See B.1.

14   pragma Import( [Convention =>] convention_identifier, [Entity =>] local_
name [, [External_Name =>] string_expression] [, [Link_Name =>]
string_expression]); -- See B.1.

15   pragma Inline(name {, name}); -- See 6.3.2.

16   pragma Inspection_Point[(object_name {, object_name})]; -- See H.3.2.

17   pragma Interrupt_Handler(handler_name); -- See C.3.1.

18   pragma Interrupt_Priority[(expression)]; -- See D.1.

19   pragma Linker_Options(string_expression); -- See B.1.

20   pragma List(identifier); -- See 2.8.

21   pragma Locking_Policy(policy_identifier); -- See D.3.

22   pragma Normalize_Scalars; -- See H.1.

23   pragma Optimize(identifier); -- See 2.8.

24   pragma Pack(first_subtype_local_name); -- See 13.2.

25   pragma Page; -- See 2.8.

26   pragma Preelaborate[(library_unit_name)]; -- See 10.2.1.

27   pragma Priority(expression); -- See D.1.

28   pragma Pure[(library_unit_name)]; -- See 10.2.1.

29   pragma Queuing_Policy(policy_identifier); -- See D.4.

30   pragma Remote_Call_Interface[(library_unit_name)]; -- See E.2.3.

31   pragma Remote_Types[(library_unit_name)]; -- See E.2.2.

32   pragma Restrictions(restriction{, restriction}); -- See 13.12.

33   pragma Reviewable; -- See H.3.1.

34   pragma Shared_Passive[(library_unit_name)]; -- See E.2.1.

35   pragma Storage_Size(expression); -- See 13.3.

36   pragma Suppress(identifier [, [On =>] name]); -- See 11.5.

37   pragma Task_Dispatching_Policy(policy_identifier ); -- See D.2.2.

38   pragma Volatile(local_name); -- See C.6.

39   pragma Volatile_Components(array_local_name); -- See C.6.


                         Wording Changes From Ada 83

        39.a   Pragmas List, Page, and Optimize are now officially defined in
        2.8, ``Pragmas''.



                                   Annex M
                                (informative)


                    Implementation-Defined Characteristics



1   {94-4693.q} {implementation defined (summary of characteristics)} The Ada
language allows for certain machine dependences in a controlled manner.
{documentation (required of an implementation)} Each Ada implementation must
document all implementation-defined characteristics:

        1.a   Ramification:  {unspecified} {specified (not!)} It need not
        document unspecified characteristics.

        1.b   Some of the items in this list require documentation only for
        implementations that conform to Specialized Needs Annexes.

    2  Whether or not each recommendation given in Implementation Advice
       is followed.  See 1.1.2(37).

    3  Capacity limitations of the implementation.  See 1.1.3(3).

    4  Variations from the standard that are impractical to avoid given
       the implementation's execution environment.  See 1.1.3(6).

    5  Which code_statements cause external interactions.  See
       1.1.3(10).

    6  The coded representation for the text of an Ada program.  See
       2.1(4).

    7  The control functions allowed in comments.  See 2.1(14).

    8  The representation for an end of line.  See 2.2(2).

    9  Maximum supported line length and lexical element length.  See
       2.2(15).

   10  Implementation-defined pragmas.  See 2.8(14).

   11  Effect of pragma Optimize.  See 2.8(27).

   12  The sequence of characters of the value returned by S'Image when
       some of the graphic characters of S'Wide_Image are not defined in
       Character.  See 3.5(37).

   13  The predefined integer types declared in Standard.  See
       3.5.4(25).

   14  Any nonstandard integer types and the operators defined for them.
       See 3.5.4(26).

   15  Any nonstandard real types and the operators defined for them.
       See 3.5.6(8).

   16  What combinations of requested decimal precision and range are
       supported for floating point types.  See 3.5.7(7).

   17  The predefined floating point types declared in Standard.  See
       3.5.7(16).

   18  The small of an ordinary fixed point type.  See 3.5.9(8).

   19  What combinations of small, range, and digits are supported for
       fixed point types.  See 3.5.9(10).

   20  The result of Tags.Expanded_Name for types declared within an
       unnamed block_statement.  See 3.9(10).

   21  Implementation-defined attributes.  See 4.1.4(12).

   22  Any implementation-defined time types.  See 9.6(6).

   23  The time base associated with relative delays.  See 9.6(20).

   24  The time base of the type Calendar.Time.  See 9.6(23).

   25  The timezone used for package Calendar operations.  See 9.6(24).

   26  Any limit on delay_until_statements of select_statements.  See
       9.6(29).

   27  Whether or not two nonoverlapping parts of a composite object are
       independently addressable, in the case where packing, record
       layout, or Component_Size is specified for the object.  See
       9.10(1).

   28  The representation for a compilation.  See 10.1(2).

   29  Any restrictions on compilations that contain multiple
       compilation_units.  See 10.1(4).

   30  The mechanisms for creating an environment and for adding and
       replacing compilation units.  See 10.1.4(3).

   31  The manner of explicitly assigning library units to a partition.
       See 10.2(2).

   32  The implementation-defined means, if any, of specifying which
       compilation units are needed by a given compilation unit.  See
       10.2(2).

   33  The manner of designating the main subprogram of a partition.
       See 10.2(7).

   34  The order of elaboration of library_items.  See 10.2(18).

   35  Parameter passing and function return for the main subprogram.
       See 10.2(21).

   36  The mechanisms for building and running partitions.  See
       10.2(24).

   37  The details of program execution, including program termination.
       See 10.2(25).

   38  The semantics of any nonactive partitions supported by the
       implementation.  See 10.2(28).

   39  The information returned by Exception_Message.  See 11.4.1(10).

   40  The result of Exceptions.Exception_Name for types declared within
       an unnamed block_statement.  See 11.4.1(12).

   41  The information returned by Exception_Information.  See
       11.4.1(13).

   42  Implementation-defined check names.  See 11.5(27).

   43  The interpretation of each aspect of representation.  See
       13.1(20).

   44  Any restrictions placed upon representation items.  See 13.1(20).

   45  The meaning of Size for indefinite subtypes.  See 13.3(48).

   46  The default external representation for a type tag.  See
       13.3(75).

   47  What determines whether a compilation unit is the same in two
       different partitions.  See 13.3(76).

   48  Implementation-defined components.  See 13.5.1(15).

   49  If Word_Size = Storage_Unit, the default bit ordering.  See
       13.5.3(5).

   50  The contents of the visible part of package System and its
       language-defined children.  See 13.7(2).

   51  The contents of the visible part of package System.Machine_Code,
       and the meaning of code_statements.  See 13.8(7).

   52  The effect of unchecked conversion.  See 13.9(11).

   53  The manner of choosing a storage pool for an access type when
       Storage_Pool is not specified for the type.  See 13.11(17).

   54  Whether or not the implementation provides user-accessible names
       for the standard pool type(s).  See 13.11(17).

   55  The meaning of Storage_Size.  See 13.11(18).

   56  Implementation-defined aspects of storage pools.  See 13.11(22).

   57  The set of restrictions allowed in a pragma Restrictions.  See
       13.12(7).

   58  The consequences of violating limitations on Restrictions
       pragmas.  See 13.12(9).

   59  The representation used by the Read and Write attributes of
       elementary types in terms of stream elements.  See 13.13.2(9).

   60  The names and characteristics of the numeric subtypes declared in
       the visible part of package Standard.  See A.1(3).

   61  The accuracy actually achieved by the elementary functions.  See
       A.5.1(1).

   62  The sign of a zero result from some of the operators or functions
       in Numerics.Generic_Elementary_Functions, when Float_Type'Signed_
       Zeros is True.  See A.5.1(46).

   63  The value of Numerics.Float_Random.Max_Image_Width.  See
       A.5.2(27).

   64  The value of Numerics.Discrete_Random.Max_Image_Width.  See
       A.5.2(27).

   65  The algorithms for random number generation.  See A.5.2(32).

   66  The string representation of a random number generator's state.
       See A.5.2(38).

   67  The minimum time interval between calls to the time-dependent
       Reset procedure that are guaranteed to initiate different random
       number sequences.  See A.5.2(45).

   68  The values of the Model_Mantissa, Model_Emin, Model_Epsilon,
       Model, Safe_First, and Safe_Last attributes, if the Numerics
       Annex is not supported.  See A.5.3(72).

   69  Any implementation-defined characteristics of the input-output
       packages.  See A.7(14).

   70  The value of Buffer_Size in Storage_IO.  See A.9(10).

   71  external files for standard input, standard output, and standard
       error See A.10(5).

   72  The accuracy of the value produced by Put.  See A.10.9(36).

   73  The meaning of Argument_Count, Argument, and Command_Name.  See
       A.15(1).

   74  Implementation-defined convention names.  See B.1(11).

   75  The meaning of link names.  See B.1(36).

   76  The manner of choosing link names when neither the link name nor
       the address of an imported or exported entity is specified.  See
       B.1(36).

   77  The effect of pragma Linker_Options.  See B.1(37).

   78  The contents of the visible part of package Interfaces and its
       language-defined descendants.  See B.2(1).

   79  Implementation-defined children of package Interfaces.  The
       contents of the visible part of package Interfaces.  See B.2(11).

   80  The types Floating, Long_Floating, Binary, Long_Binary, Decimal_
       Element, and COBOL_Character; and the initializations of the
       variables Ada_To_COBOL and COBOL_To_Ada, in Interfaces.COBOL See
       B.4(50).

   81  Support for access to machine instructions.  See C.1(1).

   82  Implementation-defined aspects of access to machine operations.
       See C.1(9).

   83  Implementation-defined aspects of interrupts.  See C.3(2).

   84  Implementation-defined aspects of preelaboration.  See C.4(13).

   85  The semantics of pragma Discard_Names.  See C.5(7).

   86  The result of the Task_Identification.Image attribute.  See
       C.7.1(7).

   87  The value of Current_Task when in a protected entry or interrupt
       handler.  See C.7.1(17).

   88  The effect of calling Current_Task from an entry body or
       interrupt handler.  See C.7.1(19).

   89  Implementation-defined aspects of Task_Attributes.  See
       C.7.2(19).

   90  Values of all Metrics.  See D(2).

   91  The declarations of Any_Priority and Priority.  See D.1(11).

   92  Implementation-defined execution resources.  See D.1(15).

   93  Whether, on a multiprocessor, a task that is waiting for access
       to a protected object keeps its processor busy.  See D.2.1(3).

   94  The affect of implementation defined execution resources on task
       dispatching.  See D.2.1(9).

   95  Implementation-defined policy_identifiers allowed in a pragma
       Task_Dispatching_Policy.  See D.2.2(3).

   96  Implementation-defined aspects of priority inversion.  See
       D.2.2(16).

   97  Implementation defined task dispatching.  See D.2.2(18).

   98  Implementation-defined policy_identifiers allowed in a pragma
       Locking_Policy.  See D.3(4).

   99  Default ceiling priorities.  See D.3(10).

  100  The ceiling of any protected object used internally by the
       implementation.  See D.3(16).

  101  Implementation-defined queuing policies.  See D.4(1).

  102  On a multiprocessor, any conditions that cause the completion of
       an aborted construct to be delayed later than what is specified
       for a single processor.  See D.6(3).

  103  Any operations that implicitly require heap storage allocation.
       See D.7(8).

  104  Implementation-defined aspects of pragma Restrictions.  See
       D.7(20).

  105  Implementation-defined aspects of package Real_Time.  See
       D.8(17).

  106  Implementation-defined aspects of delay_statements.  See D.9(8).

  107  The upper bound on the duration of interrupt blocking caused by
       the implementation.  See D.12(5).

  108  The means for creating and executing distributed programs.  See
       E(5).

  109  Any events that can result in a partition becoming inaccessible.
       See E.1(7).

  110  The scheduling policies, treatment of priorities, and management
       of shared resources between partitions in certain cases.  See
       E.1(11).

  111  Events that cause the version of a compilation unit to change.
       See E.3(5).

  112  Whether the execution of the remote subprogram is immediately
       aborted as a result of cancellation.  See E.4(13).

  113  Implementation-defined aspects of the PCS.  See E.5(25).

  114  Implementation-defined interfaces in the PCS.  See E.5(26).

  115  The values of named numbers in the package Decimal.  See F.2(7).

  116  The value of Max_Picture_Length in the package Text_IO.Editing
       See F.3.3(16).

  117  The value of Max_Picture_Length in the package Wide_
       Text_IO.Editing See F.3.4(5).

  118  The accuracy actually achieved by the complex elementary
       functions and by other complex arithmetic operations.  See
       G.1(1).

  119  The sign of a zero result (or a component thereof) from any
       operator or function in Numerics.Generic_Complex_Types, when
       Real'Signed_Zeros is True.  See G.1.1(53).

  120  The sign of a zero result (or a component thereof) from any
       operator or function in Numerics.Generic_Complex_Elementary_
       Functions, when Complex_Types.Real'Signed_Zeros is True.  See
       G.1.2(45).

  121  Whether the strict mode or the relaxed mode is the default.  See
       G.2(2).

  122  The result interval in certain cases of fixed-to-float
       conversion.  See G.2.1(10).

  123  The result of a floating point arithmetic operation in overflow
       situations, when the Machine_Overflows attribute of the result
       type is False.  See G.2.1(13).

  124  The result interval for division (or exponentiation by a negative
       exponent), when the floating point hardware implements division
       as multiplication by a reciprocal.  See G.2.1(16).

  125  The definition of close result set, which determines the accuracy
       of certain fixed point multiplications and divisions.  See
       G.2.3(5).

  126  Conditions on a universal_real operand of a fixed point
       multiplication or division for which the result shall be in the
       perfect result set.  See G.2.3(22).

  127  The result of a fixed point arithmetic operation in overflow
       situations, when the Machine_Overflows attribute of the result
       type is False.  See G.2.3(27).

  128  The result of an elementary function reference in overflow
       situations, when the Machine_Overflows attribute of the result
       type is False.  See G.2.4(4).

  129  The value of the angle threshold, within which certain elementary
       functions, complex arithmetic operations, and complex elementary
       functions yield results conforming to a maximum relative error
       bound.  See G.2.4(10).

  130  The accuracy of certain elementary functions for parameters
       beyond the angle threshold.  See G.2.4(10).

  131  The result of a complex arithmetic operation or complex
       elementary function reference in overflow situations, when the
       Machine_Overflows attribute of the corresponding real type is
       False.  See G.2.6(5).

  132  The accuracy of certain complex arithmetic operations and certain
       complex elementary functions for parameters (or components
       thereof) beyond the angle threshold.  See G.2.6(8).

  133  Information regarding bounded errors and erroneous execution.
       See H.2(1).

  134  Implementation-defined aspects of pragma Inspection_Point.  See
       H.3.2(8).

  135  Implementation-defined aspects of pragma Restrictions.  See
       H.4(25).

  136  Any restrictions on pragma Restrictions.  See H.4(27).



                                   Annex N
                                (informative)


                                   Glossary



1   {Glossary} This Annex contains informal descriptions of some terms used
in this International Standard.  To find more formal definitions, look the
term up in the index.  {94-4693.r}

2   Access type.  {Access type} An access type has values that designate
aliased objects.  Access types correspond to ``pointer types'' or ``reference
types'' in some other languages.

3   Aliased.  {Aliased} An aliased view of an object is one that can be
designated by an access value.  Objects allocated by allocators are aliased.
Objects can also be explicitly declared as aliased with the reserved word
aliased.  The Access attribute can be used to create an access value
designating an aliased object.

4   Array type.  {Array type} An array type is a composite type whose
components are all of the same type.  Components are selected by indexing.

5   Character type.  {Character type} A character type is an enumeration type
whose values include characters.

6   Class.  {Class} {closed under derivation} A class is a set of types that
is closed under derivation, which means that if a given type is in the class,
then all types derived from that type are also in the class.  The set of
types of a class share common properties, such as their primitive operations.

7   Compilation unit.  {Compilation unit} The text of a program can be
submitted to the compiler in one or more compilations.  Each compilation is a
succession of compilation_units.  A compilation_unit contains either the
declaration, the body, or a renaming of a program unit.

8   Composite type.  {Composite type} A composite type has components.

9   Construct.  {Construct} A construct is a piece of text (explicit or
implicit) that is an instance of a syntactic category defined under
``Syntax.''

10   Controlled type.  {Controlled type} A controlled type supports
user-defined assignment and finalization.  Objects are always finalized
before being destroyed.

11   Declaration.  {Declaration} A declaration is a language construct that
associates a name with (a view of) an entity.  {explicit declaration}
{implicit declaration} A declaration may appear explicitly in the program
text (an explicit declaration), or may be supposed to occur at a given place
in the text as a consequence of the semantics of another construct (an
implicit declaration).

12   Definition.  {Definition} {view} All declarations contain a definition
for a view of an entity.  A view consists of an identification of the entity
(the entity of the view), plus view-specific characteristics that affect the
use of the entity through that view (such as mode of access to an object,
formal parameter names and defaults for a subprogram, or visibility to
components of a type).  In most cases, a declaration also contains the
definition for the entity itself (a renaming_declaration is an example of a
declaration that does not define a new entity, but instead defines a view of
an existing entity (see 8.5)).

13   Derived type.  {Derived type} A derived type is a type defined in terms
of another type, which is the parent type of the derived type.  Each class
containing the parent type also contains the derived type.  The derived type
inherits properties such as components and primitive operations from the
parent.  A type together with the types derived from it (directly or
indirectly) form a derivation class.

14   Discrete type.  {Discrete type} A discrete type is either an integer
type or an enumeration type.  Discrete types may be used, for example, in
case_statements and as array indices.

15   Discriminant.  {Discriminant} A discriminant is a parameter of a
composite type.  It can control, for example, the bounds of a component of
the type if that type is an array type.  A discriminant of a task type can be
used to pass data to a task of the type upon creation.

16   Elementary type.  {Elementary type} An elementary type does not have
components.

17   Enumeration type.  {Enumeration type} An enumeration type is defined by
an enumeration of its values, which may be named by identifiers or character
literals.

18   Exception.  {Exception} An exception represents a kind of exceptional
situation; an occurrence of such a situation (at run time) is called an
exception occurrence.[ {raise [an exception]} To raise an exception is to
abandon normal program execution so as to draw attention to the fact that the
corresponding situation has arisen.  {handle [an exception]} Performing some
actions in response to the arising of an exception is called handling the
exception.]

19   Execution.  {Execution} The process by which a construct achieves its
run-time effect is called execution.  {elaboration} {evaluation} Execution of
a declaration is also called elaboration.  Execution of an expression is also
called evaluation.

20   Generic unit.  {Generic unit} A generic unit is a template for a
(nongeneric) program unit; the template can be parameterized by objects,
types, subprograms, and packages.  An instance of a generic unit is created
by a generic_instantiation.  The rules of the language are enforced when a
generic unit is compiled, using a generic contract model; additional checks
are performed upon instantiation to verify the contract is met.  That is, the
declaration of a generic unit represents a contract between the body of the
generic and instances of the generic.  Generic units can be used to perform
the role that macros sometimed play in other languages.

21   Integer type.  {Integer type} Integer types comprise the signed integer
types and the modular types.  A signed integer type has a base range that
includes both positive and negative numbers, and has operations that may
raise an exception when the result is outside the base range.  A modular type
has a base range whose lower bound is zero, and has operations with
``wraparound'' semantics.  Modular types subsume what are called ``unsigned
types'' in some other languages.

22   Library unit.  {Library unit} A library unit is a separately compiled
program unit, and is always a package, subprogram, or generic unit.
{94-4599.f} Library units may have other (logically nested) library units as
children, and may have other program units physically nested within them.
{subsystem} A root library unit, together with its children and grandchildren
and so on, form a subsystem.

23   Limited type.  {Limited type} A limited type is (a view of) a type for
which the assignment operation is not allowed.  A nonlimited type is a (view
of a) type for which the assignment operation is allowed.

24   Object.  {Object} An object is either a constant or a variable.  An
object contains a value.  An object is created by an object_declaration or by
an allocator.  A formal parameter is (a view of) an object.  A subcomponent
of an object is an object.

25   Package.  {Package} Packages are program units that allow the
specification of groups of logically related entities.  Typically, a package
contains the declaration of a type (often a private type or private
extension) along with the declarations of primitive subprograms of the type,
which can be called from outside the package, while their inner workings
remain hidden from outside users.

26   Partition.  {Partition} A partition is a part of a program.  Each
partition consists of a set of library units.  Each partition may run in a
separate address space, possibly on a separate computer.  A program may
contain just one partition.  A distributed program typically contains
multiple partitions, which can execute concurrently.

27   Pragma.  {Pragma} A pragma is a compiler directive.  There are
language-defined pragmas that give instructions for optimization, listing
control, etc.  An implementation may support additional (implementation-
defined) pragmas.

28   Primitive operations.  {Primitive operations} The primitive operations
of a type are the operations (such as subprograms) declared together with the
type declaration.  They are inherited by other types in the same class of
types.  For a tagged type, the primitive subprograms are dispatching
subprograms, providing run-time polymorphism.  A dispatching subprogram may
be called with statically tagged operands, in which case the subprogram body
invoked is determined at compile time.  Alternatively, a dispatching
subprogram may be called using a dispatching call, in which case the
subprogram body invoked is determined at run time.

29   Private extension.  {Private extension} A private extension is like a
record extension, except that the components of the extension part are hidden
from its clients.

30   Private type.  {Private type} A private type is a partial view of a type
whose full view is hidden from its clients.

31   Program unit.  {Program unit} A program unit is either a package, a task
unit, a protected unit, a protected entry, a generic unit, or an explicitly
declared subprogram other than an enumeration literal.  Certain kinds of
program units can be separately compiled.  Alternatively, they can appear
physically nested within other program units.

32   Program.  {Program} A program is a set of partitions, each of which may
execute in a separate address space, possibly on a separate computer.  A
partition consists of a set of library units.

33   Protected type.  {Protected type} A protected type is a composite type
whose components are protected from concurrent access by multiple tasks.

34   Real type.  {Real type} A real type has values that are approximations
of the real numbers.  Floating point and fixed point types are real types.

35   Record extension.  {Record extension} A record extension is a type that
extends another type by adding additional components.

36   Record type.  {Record type} A record type is a composite type consisting
of zero or more named components, possibly of different types.

37   Scalar type.  {Scalar type} A scalar type is either a discrete type or a
real type.

38   Subtype.  {Subtype} A subtype is a type together with a constraint,
which constrains the values of the subtype to satisfy a certain condition.
The values of a subtype are a subset of the values of its type.

39   Tagged type.  {Tagged type} The objects of a tagged type have a run-time
type tag, which indicates the specific type with which the object was
originally created.  An operand of a class-wide tagged type can be used in a
dispatching call; the tag indicates which subprogram body to invoke.
Nondispatching calls, in which the subprogram body to invoke is determined at
compile time, are also allowed.  Tagged types may be extended with additional
components.

40   Task type.  {Task type} A task type is a composite type whose values are
tasks, which are active entities that may execute concurrently with other
tasks.  The top-level task of a partition is called the environment task.

41   Type.  {Type} Each object has a type.  A type has an associated set of
values, and a set of primitive operations which implement the fundamental
aspects of its semantics.  Types are grouped into classes.  The types of a
given class share a set of primitive operations.  {closed under derivation}
Classes are closed under derivation; that is, if a type is in a class, then
all of its derivatives are in that class.

42   View.  {View} (See Definition.)



                                   Annex P
                                (informative)


                                Syntax Summary



1   {syntax (complete listing)} {grammar (complete listing)} {context free
grammar (complete listing)} {BNF (Backus-Naur Form) (complete listing)}
{Backus-Naur Form (BNF) (complete listing)} This Annex summarizes the
complete syntax of the language.  See 1.1.4 for a description of the notation
used.  {94-4693.s}


    2.1:
    character ::= graphic_character | format_effector | other_control_function

    2.1:
    graphic_character ::= identifier_letter | digit | space_character | special\
_character

    2.3:
    identifier ::=
       identifier_letter {[underline] letter_or_digit}

    2.3:
    letter_or_digit ::= identifier_letter | digit

    2.4:
    numeric_literal ::= decimal_literal | based_literal

    2.4.1:
    decimal_literal ::= numeral [.numeral] [exponent]

    2.4.1:
    numeral ::= digit {[underline] digit}

    2.4.1:
    exponent ::= E [+] numeral | E - numeral

    2.4.2:
    based_literal ::=
       base # based_numeral [.based_numeral] # [exponent]

    2.4.2:
    base ::= numeral

    2.4.2:
    based_numeral ::=
       extended_digit {[underline] extended_digit}

    2.4.2:
    extended_digit ::= digit | A | B | C | D | E | F

    2.5:
    character_literal ::= 'graphic_character'

    2.6:
    string_literal ::= "{string_element}"

    2.6:
    string_element ::= "" | non_quotation_mark_graphic_character

    A string_element is either a pair of quotation marks (""),
    or a single graphic_character other than a quotation mark.

    2.7:
    comment ::= --{non_end_of_line_character}

    2.8:
    pragma ::=
       pragma identifier [(pragma_argument_association {, pragma_argument_assoc\
iation})];

    2.8:
    pragma_argument_association ::=
         [pragma_argument_identifier =>] name
       | [pragma_argument_identifier =>] expression

    3.1:
    basic_declaration ::=
         type_declaration                 | subtype_declaration
       | object_declaration               | number_declaration
       | subprogram_declaration           | abstract_subprogram_declaration
       | package_declaration              | renaming_declaration
       | exception_declaration            | generic_declaration
       | generic_instantiation

    3.1:
    defining_identifier ::= identifier

    3.2.1:
    type_declaration ::=  full_type_declaration
       | incomplete_type_declaration
       | private_type_declaration
       | private_extension_declaration

    3.2.1:
    full_type_declaration ::=
         type defining_identifier [known_discriminant_part] is type_definition;
       | task_type_declaration
       | protected_type_declaration

    3.2.1:
    type_definition ::=
         enumeration_type_definition | integer_type_definition
       | real_type_definition        | array_type_definition
       | record_type_definition      | access_type_definition
       | derived_type_definition

    3.2.2:
    subtype_declaration ::=
       subtype defining_identifier is subtype_indication;

    3.2.2:
    subtype_indication ::=  subtype_mark [constraint]

    3.2.2:
    subtype_mark ::= subtype_name

    3.2.2:
    constraint ::= scalar_constraint | composite_constraint

    3.2.2:
    scalar_constraint ::=
         range_constraint | digits_constraint | delta_constraint

    3.2.2:
    composite_constraint ::=
         index_constraint | discriminant_constraint

    3.3.1:
    object_declaration ::=
        defining_identifier_list : [aliased] [constant] subtype_indication [:= \
expression];
      | defining_identifier_list : [aliased] [constant] array_type_definition [\
:= expression];
      | single_task_declaration
      | single_protected_declaration

    3.3.1:
    defining_identifier_list ::=
      defining_identifier {, defining_identifier}

    3.3.2:
    number_declaration ::=
         defining_identifier_list : constant := static_expression;

    3.4:
    derived_type_definition ::= [abstract] new parent_subtype_indication [recor\
d_extension_part]

    3.5:
    range_constraint ::=  range range

    3.5:
    range ::=  range_attribute_reference
       | simple_expression .. simple_expression

    3.5.1:
    enumeration_type_definition ::=
       (enumeration_literal_specification {, enumeration_literal_specification})

    3.5.1:
    enumeration_literal_specification ::=  defining_identifier | defining_chara\
cter_literal

    3.5.1:
    defining_character_literal ::= character_literal

    3.5.4:
    integer_type_definition ::= signed_integer_type_definition | modular_type_d\
efinition

    3.5.4:
    signed_integer_type_definition ::= range static_simple_expression .. static\
_simple_expression

    3.5.4:
    modular_type_definition ::= mod static_expression

    3.5.6:
    real_type_definition ::=
       floating_point_definition | fixed_point_definition

    3.5.7:
    floating_point_definition ::=
      digits static_expression [real_range_specification]

    3.5.7:
    real_range_specification ::=
      range static_simple_expression .. static_simple_expression

    3.5.9:
    fixed_point_definition ::= ordinary_fixed_point_definition | decimal_fixed_\
point_definition

    3.5.9:
    ordinary_fixed_point_definition ::=
       delta static_expression  real_range_specification

    3.5.9:
    decimal_fixed_point_definition ::=
       delta static_expression digits static_expression [real_range_specificati\
on]

    3.5.9:
    digits_constraint ::=
       digits static_expression [range_constraint]

    3.6:
    array_type_definition ::=
       unconstrained_array_definition | constrained_array_definition

    3.6:
    unconstrained_array_definition ::=
       array(index_subtype_definition {, index_subtype_definition}) of componen\
t_definition

    3.6:
    index_subtype_definition ::= subtype_mark range <>

    3.6:
    constrained_array_definition ::=
       array (discrete_subtype_definition {, discrete_subtype_definition}) of c\
omponent_definition

    3.6:
    discrete_subtype_definition ::= discrete_subtype_indication | range

    3.6:
    component_definition ::= [aliased] subtype_indication

    3.6.1:
    index_constraint ::=  (discrete_range {, discrete_range})

    3.6.1:
    discrete_range ::= discrete_subtype_indication | range

    3.7:
    discriminant_part ::= unknown_discriminant_part | known_discriminant_part

    3.7:
    unknown_discriminant_part ::= (<>)

    3.7:
    known_discriminant_part ::=
       (discriminant_specification {; discriminant_specification})

    3.7:
    discriminant_specification ::=
       defining_identifier_list : subtype_mark [:= default_expression]
     | defining_identifier_list : access_definition [:= default_expression]

    3.7:
    default_expression ::= expression

    3.7.1:
    discriminant_constraint ::=
       (discriminant_association {, discriminant_association})

    3.7.1:
    discriminant_association ::=
       [discriminant_selector_name {| discriminant_selector_name} =>] expression

    3.8:
    record_type_definition ::= [[abstract] tagged] [limited] record_definition

    3.8:
    record_definition ::=
        record
           component_list
        end record
      | null record

    3.8:
    component_list ::=
          component_item {component_item}
       | {component_item} variant_part
       |  null;

    3.8:
    component_item ::= component_declaration | representation_clause

    3.8:
    component_declaration ::=
       defining_identifier_list : component_definition [:= default_expression];

    3.8.1:
    variant_part ::=
       case discriminant_direct_name is
           variant
          {variant}
       end case;

    3.8.1:
    variant ::=
       when discrete_choice_list =>
          component_list

    3.8.1:
    discrete_choice_list ::= discrete_choice {| discrete_choice}

    3.8.1:
    discrete_choice ::= expression | discrete_range | others

    3.9.1:
    record_extension_part ::= with record_definition

    3.10:
    access_type_definition ::=
        access_to_object_definition
      | access_to_subprogram_definition

    3.10:
    access_to_object_definition ::=
        access [general_access_modifier] subtype_indication

    3.10:
    general_access_modifier ::= all | constant

    3.10:
    access_to_subprogram_definition ::=
        access [protected] procedure parameter_profile
      | access [protected] function  parameter_and_result_profile

    3.10:
    access_definition ::= access subtype_mark

    3.10.1:
    incomplete_type_declaration ::= type defining_identifier [discriminant_part\
];

    3.11:
    declarative_part ::= {declarative_item}

    3.11:
    declarative_item ::=
        basic_declarative_item | body

    3.11:
    basic_declarative_item ::=
        basic_declaration | representation_clause | use_clause

    3.11:
    body ::= proper_body | body_stub

    3.11:
    proper_body ::=
        subprogram_body | package_body | task_body | protected_body

    4.1:
    name ::=
         direct_name                | explicit_dereference
       | indexed_component          | slice
       | selected_component         | attribute_reference
       | type_conversion            | function_call
       | character_literal

    4.1:
    direct_name ::= identifier | operator_symbol

    4.1:
    prefix ::= name | implicit_dereference

    4.1:
    explicit_dereference ::= name.all

    4.1:
    implicit_dereference ::= name

    4.1.1:
    indexed_component ::= prefix(expression {, expression})

    4.1.2:
    slice ::= prefix(discrete_range)

    4.1.3:
    selected_component ::= prefix . selector_name

    4.1.3:
    selector_name ::= identifier | character_literal | operator_symbol

    4.1.4:
    attribute_reference ::= prefix'attribute_designator

    4.1.4:
    attribute_designator ::=
        identifier[(static_expression)]
      | Access | Delta | Digits

    4.1.4:
    range_attribute_reference ::= prefix'range_attribute_designator

    4.1.4:
    range_attribute_designator ::= Range[(static_expression)]

    4.3:
    aggregate ::= record_aggregate | extension_aggregate | array_aggregate

    4.3.1:
    record_aggregate ::= (record_component_association_list)

    4.3.1:
    record_component_association_list ::=
        record_component_association {, record_component_association}
      | null record

    4.3.1:
    record_component_association ::=
       [ component_choice_list => ] expression

    4.3.1:
    component_choice_list ::=
         component_selector_name {| component_selector_name}
       | others

    4.3.2:
    extension_aggregate ::=
        (ancestor_part with record_component_association_list)

    4.3.2:
    ancestor_part ::= expression | subtype_mark

    4.3.3:
    array_aggregate ::=
      positional_array_aggregate | named_array_aggregate

    4.3.3:
    positional_array_aggregate ::=
        (expression, expression {, expression})
      | (expression {, expression}, others => expression)

    4.3.3:
    named_array_aggregate ::=
        (array_component_association {, array_component_association})

    4.3.3:
    array_component_association ::=
        discrete_choice_list => expression

    4.4:
    expression ::=
         relation {and relation} | relation {and then relation}
       | relation {or relation}  | relation {or else relation}
       | relation {xor relation}

    4.4:
    relation ::=
         simple_expression [relational_operator simple_expression]
       | simple_expression [not] in range
       | simple_expression [not] in subtype_mark

    4.4:
    simple_expression ::= [unary_adding_operator] term {binary_adding_operator \
term}

    4.4:
    term ::= factor {multiplying_operator factor}

    4.4:
    factor ::= primary [** primary] | abs primary | not primary

    4.4:
    primary ::=
       numeric_literal | null | string_literal | aggregate
     | name | qualified_expression | allocator | (expression)

    4.5:
    logical_operator                                      ::=  and | or  | xor

    4.5:
    relational_operator          ::=  =   | /=  | <   | <= | > | >=

    4.5:
    binary_adding_operator       ::=  +   | -   | &

    4.5:
    unary_adding_operator        ::=  +   | -

    4.5:
    multiplying_operator         ::=  *   | /   | mod | rem

    4.5:
    highest_precedence_operator     ::=  **  | abs | not

    4.6:
    type_conversion ::=
        subtype_mark(expression)
      | subtype_mark(name)

    4.7:
    qualified_expression ::=
       subtype_mark'(expression) | subtype_mark'aggregate

    4.8:
    allocator ::=
       new subtype_indication | new qualified_expression

    5.1:
    sequence_of_statements ::= statement {statement}

    5.1:
    statement ::=
       {label} simple_statement | {label} compound_statement

    5.1:
    simple_statement ::= null_statement
       | assignment_statement              | exit_statement
       | goto_statement          | procedure_call_statement
       | return_statement        | entry_call_statement
       | requeue_statement       | delay_statement
       | abort_statement         | raise_statement
       | code_statement

    5.1:
    compound_statement ::=
         if_statement            | case_statement
       | loop_statement          | block_statement
       | accept_statement        | select_statement

    5.1:
    null_statement ::= null;

    5.1:
    label ::= <<label_statement_identifier>>

    5.1:
    statement_identifier ::= direct_name

    5.2:
    assignment_statement ::=
       variable_name := expression;

    5.3:
    if_statement ::=
        if condition then
          sequence_of_statements
       {elsif condition then
          sequence_of_statements}
       [else
          sequence_of_statements]
        end if;

    5.3:
    condition ::= boolean_expression

    5.4:
    case_statement ::=
       case expression is
           case_statement_alternative
          {case_statement_alternative}
       end case;

    5.4:
    case_statement_alternative ::=
       when discrete_choice_list =>
          sequence_of_statements

    5.5:
    loop_statement ::=
       [loop_statement_identifier:]
          [iteration_scheme] loop
             sequence_of_statements
           end loop [loop_identifier];

    5.5:
    iteration_scheme ::= while condition
       | for loop_parameter_specification

    5.5:
    loop_parameter_specification ::=
       defining_identifier in [reverse] discrete_subtype_definition

    5.6:
    block_statement ::=
       [block_statement_identifier:]
           [declare
                declarative_part]
            begin
                handled_sequence_of_statements
            end [block_identifier];

    5.7:
    exit_statement ::=
       exit [loop_name] [when condition];

    5.8:
    goto_statement ::= goto label_name;

    6.1:
    subprogram_declaration ::= subprogram_specification;

    6.1:
    abstract_subprogram_declaration ::= subprogram_specification is abstract;

    6.1:
    subprogram_specification ::=
         procedure defining_program_unit_name  parameter_profile
       | function defining_designator  parameter_and_result_profile

    6.1:
    designator ::= [parent_unit_name . ]identifier | operator_symbol

    6.1:
    defining_designator ::= defining_program_unit_name | defining_operator_symb\
ol

    6.1:
    defining_program_unit_name ::= [parent_unit_name . ]defining_identifier

    6.1:
    operator_symbol ::= string_literal

    6.1:
    defining_operator_symbol ::= operator_symbol

    6.1:
    parameter_profile ::= [formal_part]

    6.1:
    parameter_and_result_profile ::= [formal_part] return subtype_mark

    6.1:
    formal_part ::=
       (parameter_specification {; parameter_specification})

    6.1:
    parameter_specification ::=
        defining_identifier_list : mode  subtype_mark [:= default_expression]
      | defining_identifier_list : access_definition [:= default_expression]

    6.1:
    mode ::= [in] | in out | out

    6.3:
    subprogram_body ::=
        subprogram_specification is
           declarative_part
        begin
            handled_sequence_of_statements
        end [designator];

    6.4:
    procedure_call_statement ::=
        procedure_name;
      | procedure_prefix actual_parameter_part;

    6.4:
    function_call ::=
        function_name
      | function_prefix actual_parameter_part

    6.4:
    actual_parameter_part ::=
        (parameter_association {, parameter_association})

    6.4:
    parameter_association ::=
       [formal_parameter_selector_name =>] explicit_actual_parameter

    6.4:
    explicit_actual_parameter ::= expression | variable_name

    6.5:
    return_statement ::= return [expression];

    7.1:
    package_declaration ::= package_specification;

    7.1:
    package_specification ::=
        package defining_program_unit_name is
          {basic_declarative_item}
       [private
          {basic_declarative_item}]
        end [[parent_unit_name.]identifier]

    7.2:
    package_body ::=
        package body defining_program_unit_name is
           declarative_part
       [begin
            handled_sequence_of_statements]
        end [[parent_unit_name.]identifier];

    7.3:
    private_type_declaration ::=
       type defining_identifier [discriminant_part] is [[abstract] tagged] [lim\
ited] private;

    7.3:
    private_extension_declaration ::=
       type defining_identifier [discriminant_part] is
         [abstract] new ancestor_subtype_indication with private;

    8.4:
    use_clause ::= use_package_clause | use_type_clause

    8.4:
    use_package_clause ::= use package_name {, package_name};

    8.4:
    use_type_clause ::= use type subtype_mark {, subtype_mark};

    8.5:
    renaming_declaration ::=
          object_renaming_declaration
        | exception_renaming_declaration
        | package_renaming_declaration
        | subprogram_renaming_declaration
        | generic_renaming_declaration

    8.5.1:
    object_renaming_declaration ::= defining_identifier : subtype_mark renames \
object_name;

    8.5.2:
    exception_renaming_declaration ::= defining_identifier : exception renames \
exception_name;

    8.5.3:
    package_renaming_declaration ::= package defining_program_unit_name renames\
 package_name;

    8.5.4:
    subprogram_renaming_declaration ::= subprogram_specification renames callab\
le_entity_name;

    8.5.5:
    generic_renaming_declaration ::=
        generic package       defining_program_unit_name renames generic_packag\
e_name;
      | generic procedure     defining_program_unit_name renames generic_proced\
ure_name;
      | generic function      defining_program_unit_name renames generic_functi\
on_name;

    9.1:
    task_type_declaration ::=
       task type defining_identifier [known_discriminant_part] [is task_definit\
ion];

    9.1:
    single_task_declaration ::=
       task defining_identifier [is task_definition];

    9.1:
    task_definition ::=
         {task_item}
      [ private
         {task_item}]
      end [task_identifier]

    9.1:
    task_item ::= entry_declaration | representation_clause

    9.1:
    task_body ::=
       task body defining_identifier is
         declarative_part
       begin
         handled_sequence_of_statements
       end [task_identifier];

    9.4:
    protected_type_declaration ::=
      protected type defining_identifier [known_discriminant_part] is protected\
_definition;

    9.4:
    single_protected_declaration ::=
      protected defining_identifier is protected_definition;

    9.4:
    protected_definition ::=
        { protected_operation_declaration }
    [ private
        { protected_element_declaration } ]
      end [protected_identifier]

    9.4:
    protected_operation_declaration ::= subprogram_declaration
         | entry_declaration
         | representation_clause

    9.4:
    protected_element_declaration ::= protected_operation_declaration
         | component_declaration

    9.4:
    protected_body ::=
      protected body defining_identifier is
       { protected_operation_item }
      end [protected_identifier];

    9.4:
    protected_operation_item ::= subprogram_declaration
         | subprogram_body
         | entry_body
         | representation_clause

    9.5.2:
    entry_declaration ::=
       entry defining_identifier [(discrete_subtype_definition)] parameter_prof\
ile;

    9.5.2:
    accept_statement ::=
       accept entry_direct_name [(entry_index)] parameter_profile [do
         handled_sequence_of_statements
       end [entry_identifier]];

    9.5.2:
    entry_index ::= expression

    9.5.2:
    entry_body ::=
      entry defining_identifier  entry_body_formal_part  entry_barrier is
        declarative_part
      begin
        handled_sequence_of_statements
      end [entry_identifier];

    9.5.2:
    entry_body_formal_part ::= [(entry_index_specification)] parameter_profile

    9.5.2:
    entry_barrier ::= when condition

    9.5.2:
    entry_index_specification ::= for defining_identifier in discrete_subtype_d\
efinition

    9.5.3:
    entry_call_statement ::= entry_name [actual_parameter_part];

    9.5.4:
    requeue_statement ::= requeue entry_name [with abort];

    9.6:
    delay_statement ::= delay_until_statement | delay_relative_statement

    9.6:
    delay_until_statement ::= delay until delay_expression;

    9.6:
    delay_relative_statement ::= delay delay_expression;

    9.7:
    select_statement ::=
       selective_accept
      | timed_entry_call
      | conditional_entry_call
      | asynchronous_select

    9.7.1:
    selective_accept ::=
      select
       [guard]
         select_alternative
    { or
       [guard]
         select_alternative }
    [ else
       sequence_of_statements ]
      end select;

    9.7.1:
    guard ::= when condition =>

    9.7.1:
    select_alternative ::=
       accept_alternative
      | delay_alternative
      | terminate_alternative

    9.7.1:
    accept_alternative ::=
      accept_statement [sequence_of_statements]

    9.7.1:
    delay_alternative ::=
      delay_statement [sequence_of_statements]

    9.7.1:
    terminate_alternative ::= terminate;

    9.7.2:
    timed_entry_call ::=
      select
       entry_call_alternative
      or
       delay_alternative
      end select;

    9.7.2:
    entry_call_alternative ::=
      entry_call_statement [sequence_of_statements]

    9.7.3:
    conditional_entry_call ::=
      select
       entry_call_alternative
      else
       sequence_of_statements
      end select;

    9.7.4:
    asynchronous_select ::=
      select
       triggering_alternative
      then abort
       abortable_part
      end select;

    9.7.4:
    triggering_alternative ::= triggering_statement [sequence_of_statements]

    9.7.4:
    triggering_statement ::= entry_call_statement | delay_statement

    9.7.4:
    abortable_part ::= sequence_of_statements

    9.8:
    abort_statement ::= abort task_name {, task_name};

    10.1.1:
    compilation ::= {compilation_unit}

    10.1.1:
    compilation_unit ::=
        context_clause library_item
      | context_clause subunit

    10.1.1:
    library_item ::= [private] library_unit_declaration
      | library_unit_body
      | [private] library_unit_renaming_declaration

    10.1.1:
    library_unit_declaration ::=
         subprogram_declaration | package_declaration
       | generic_declaration  | generic_instantiation

    10.1.1:
    library_unit_renaming_declaration ::=
       package_renaming_declaration
     | generic_renaming_declaration
     | subprogram_renaming_declaration

    10.1.1:
    library_unit_body ::= subprogram_body | package_body

    10.1.1:
    parent_unit_name ::= name

    10.1.2:
    context_clause ::= {context_item}

    10.1.2:
    context_item ::= with_clause | use_clause

    10.1.2:
    with_clause ::= with library_unit_name {, library_unit_name};

    10.1.3:
    body_stub ::= subprogram_body_stub | package_body_stub | task_body_stub | p\
rotected_body_stub

    10.1.3:
    subprogram_body_stub ::= subprogram_specification is separate;

    10.1.3:
    package_body_stub ::= package body defining_identifier is separate;

    10.1.3:
    task_body_stub ::= task body defining_identifier is separate;

    10.1.3:
    protected_body_stub ::= protected body defining_identifier is separate;

    10.1.3:
    subunit ::= separate (parent_unit_name) proper_body

    11.1:
    exception_declaration ::= defining_identifier_list : exception;

    11.2:
    handled_sequence_of_statements ::=
         sequence_of_statements
      [exception
         exception_handler
        {exception_handler}]

    11.2:
    exception_handler ::=
      when [choice_parameter_specification:] exception_choice {| exception_choi\
ce} =>
         sequence_of_statements

    11.2:
    choice_parameter_specification ::= defining_identifier

    11.2:
    exception_choice ::= exception_name | others

    11.3:
    raise_statement ::= raise [exception_name];

    12.1:
    generic_declaration ::= generic_subprogram_declaration | generic_package_de\
claration

    12.1:
    generic_subprogram_declaration ::=
         generic_formal_part  subprogram_specification;

    12.1:
    generic_package_declaration ::=
         generic_formal_part  package_specification;

    12.1:
    generic_formal_part ::= generic {generic_formal_parameter_declaration | use\
_clause}

    12.1:
    generic_formal_parameter_declaration ::=
          formal_object_declaration
        | formal_type_declaration
        | formal_subprogram_declaration
        | formal_package_declaration

    12.3:
    generic_instantiation ::=
         package defining_program_unit_name is
             new generic_package_name [generic_actual_part];
       | procedure defining_program_unit_name is
             new generic_procedure_name [generic_actual_part];
       | function defining_designator is
             new generic_function_name [generic_actual_part];

    12.3:
    generic_actual_part ::=
       (generic_association {, generic_association})

    12.3:
    generic_association ::=
       [generic_formal_parameter_selector_name =>] explicit_generic_actual_para\
meter

    12.3:
    explicit_generic_actual_parameter ::= expression | variable_name
       | subprogram_name | entry_name | subtype_mark
       | package_instance_name

    12.4:
    formal_object_declaration ::=
        defining_identifier_list : mode subtype_mark [:= default_expression];

    12.5:
    formal_type_declaration ::=
        type defining_identifier[discriminant_part] is formal_type_definition;

    12.5:
    formal_type_definition ::=
          formal_private_type_definition
        | formal_derived_type_definition
        | formal_discrete_type_definition
        | formal_signed_integer_type_definition
        | formal_modular_type_definition
        | formal_floating_point_definition
        | formal_ordinary_fixed_point_definition
        | formal_decimal_fixed_point_definition
        | formal_array_type_definition
        | formal_access_type_definition

    12.5.1:
    formal_private_type_definition ::= [[abstract] tagged] [limited] private

    12.5.1:
    formal_derived_type_definition ::= [abstract] new subtype_mark [with privat\
e]

    12.5.2:
    formal_discrete_type_definition ::= (<>)

    12.5.2:
    formal_signed_integer_type_definition ::= range <>

    12.5.2:
    formal_modular_type_definition ::= mod <>

    12.5.2:
    formal_floating_point_definition ::= digits <>

    12.5.2:
    formal_ordinary_fixed_point_definition ::= delta <>

    12.5.2:
    formal_decimal_fixed_point_definition ::= delta <> digits <>

    12.5.3:
    formal_array_type_definition ::= array_type_definition

    12.5.4:
    formal_access_type_definition ::= access_type_definition

    12.6:
    formal_subprogram_declaration ::= with subprogram_specification [is subprog\
ram_default];

    12.6:
    subprogram_default ::= default_name | <>

    12.6:
    default_name ::= name

    12.7:
    formal_package_declaration ::=
        with package defining_identifier is new generic_package_name  formal_pa\
ckage_actual_part;

    12.7:
    formal_package_actual_part ::=
        (<>) | [generic_actual_part]

    13.1:
    representation_clause ::= attribute_definition_clause
          | enumeration_representation_clause
          | record_representation_clause
          | at_clause

    13.1:
    local_name ::= direct_name
          | direct_name'attribute_designator
          | library_unit_name

    13.3:
    attribute_definition_clause ::=
          for local_name'attribute_designator use expression;
        | for local_name'attribute_designator use name;

    13.4:
    enumeration_representation_clause ::=
        for first_subtype_local_name use enumeration_aggregate;

    13.4:
    enumeration_aggregate ::= array_aggregate

    13.5.1:
    record_representation_clause ::=
        for first_subtype_local_name use
          record [mod_clause]
            {component_clause}
          end record;

    13.5.1:
    component_clause ::=
        component_local_name at position range first_bit .. last_bit;

    13.5.1:
    position ::= static_expression

    13.5.1:
    first_bit ::= static_simple_expression

    13.5.1:
    last_bit ::= static_simple_expression

    13.8:
    code_statement ::= qualified_expression;

    13.12:
    restriction ::= restriction_identifier
        | restriction_parameter_identifier => expression

    J.3:
    delta_constraint ::= delta static_expression [range_constraint]

    J.7:
    at_clause ::= for direct_name use at expression;

    J.8:
    mod_clause ::= at mod static_expression;
                           SYNTAX CROSS REFERENCE

{syntax (cross reference)} {grammar (cross reference)} {context free grammar
(cross reference)} {BNF (Backus-Naur Form) (cross reference)} {Backus-Naur
Form (BNF) (cross reference)}

2


    abort_statement
       simple_statement                     5.1

    abortable_part
       asynchronous_select                  9.7.4

    abstract_subprogram_declaration
       basic_declaration                    3.1

    accept_alternative
       select_alternative                   9.7.1

    accept_statement
       accept_alternative                   9.7.1
       compound_statement                   5.1

    access_definition
       discriminant_specification           3.7
       parameter_specification              6.1

    access_type_definition
       formal_access_type_definition        12.5.4
       type_definition                      3.2.1

    access_to_object_definition
       access_type_definition               3.10

    access_to_subprogram_definition
       access_type_definition               3.10

    actual_parameter_part
       entry_call_statement                 9.5.3
       function_call                        6.4
       procedure_call_statement             6.4

    aggregate
       primary                              4.4
       qualified_expression                 4.7

    allocator
       primary                              4.4

    ancestor_part
       extension_aggregate                  4.3.2

    array_aggregate
       aggregate                            4.3
       enumeration_aggregate                13.4

    array_component_association
       named_array_aggregate                4.3.3

    array_type_definition
       formal_array_type_definition         12.5.3
       object_declaration                   3.3.1
       type_definition                      3.2.1

    assignment_statement
       simple_statement                     5.1

    asynchronous_select
       select_statement                     9.7

    at_clause
       representation_clause                13.1

    attribute_definition_clause
       representation_clause                13.1

    attribute_designator
       attribute_definition_clause          13.3
       attribute_reference                  4.1.4
       local_name                           13.1

    attribute_reference
       name                                 4.1

    base
       based_literal                        2.4.2

    based_literal
       numeric_literal                      2.4

    based_numeral
       based_literal                        2.4.2

    basic_declaration
       basic_declarative_item               3.11

    basic_declarative_item
       declarative_item                     3.11
       package_specification                7.1

    binary_adding_operator
       simple_expression                    4.4

    block_statement
       compound_statement                   5.1

    body
       declarative_item                     3.11

    body_stub
       body                                 3.11

    case_statement
       compound_statement                   5.1

    case_statement_alternative
       case_statement                       5.4

    character
       comment                              2.7

    character_literal
       defining_character_literal           3.5.1
       name                                 4.1
       selector_name                        4.1.3

    choice_parameter_specification
       exception_handler                    11.2

    code_statement
       simple_statement                     5.1

    compilation_unit
       compilation                          10.1.1

    component_choice_list
       record_component_association         4.3.1

    component_clause
       record_representation_clause         13.5.1

    component_declaration
       component_item                       3.8
       protected_element_declaration        9.4

    component_definition
       component_declaration                3.8
       constrained_array_definition         3.6
       unconstrained_array_definition       3.6

    component_item
       component_list                       3.8

    component_list
       record_definition                    3.8
       variant                              3.8.1

    composite_constraint
       constraint                           3.2.2

    compound_statement
       statement                            5.1

    condition
       entry_barrier                        9.5.2
       exit_statement                       5.7
       guard                                9.7.1
       if_statement                         5.3
       iteration_scheme                     5.5

    conditional_entry_call
       select_statement                     9.7

    constrained_array_definition
       array_type_definition                3.6

    constraint
       subtype_indication                   3.2.2

    context_clause
       compilation_unit                     10.1.1

    context_item
       context_clause                       10.1.2

    decimal_fixed_point_definition
       fixed_point_definition               3.5.9

    decimal_literal
       numeric_literal                      2.4

    declarative_item
       declarative_part                     3.11

    declarative_part
       block_statement                      5.6
       entry_body                           9.5.2
       package_body                         7.2
       subprogram_body                      6.3
       task_body                            9.1

    default_expression
       component_declaration                3.8
       discriminant_specification           3.7
       formal_object_declaration            12.4
       parameter_specification              6.1

    default_name
       subprogram_default                   12.6

    defining_character_literal
       enumeration_literal_specification    3.5.1

    defining_designator
       generic_instantiation                12.3
       subprogram_specification             6.1

    defining_identifier
       choice_parameter_specification       11.2
       defining_identifier_list             3.3.1
       defining_program_unit_name           6.1
       entry_body                           9.5.2
       entry_declaration                    9.5.2
       entry_index_specification            9.5.2
       enumeration_literal_specification    3.5.1
       exception_renaming_declaration       8.5.2
       formal_package_declaration           12.7
       formal_type_declaration              12.5
       full_type_declaration                3.2.1
       incomplete_type_declaration          3.10.1
       loop_parameter_specification         5.5
       object_renaming_declaration          8.5.1
       package_body_stub                    10.1.3
       private_extension_declaration        7.3
       private_type_declaration             7.3
       protected_body                       9.4
       protected_body_stub                  10.1.3
       protected_type_declaration           9.4
       single_protected_declaration         9.4
       single_task_declaration              9.1
       subtype_declaration                  3.2.2
       task_body                            9.1
       task_body_stub                       10.1.3
       task_type_declaration                9.1

    defining_identifier_list
       component_declaration                3.8
       discriminant_specification           3.7
       exception_declaration                11.1
       formal_object_declaration            12.4
       number_declaration                   3.3.2
       object_declaration                   3.3.1
       parameter_specification              6.1

    defining_operator_symbol
       defining_designator                  6.1

    defining_program_unit_name
       defining_designator                  6.1
       generic_instantiation                12.3
       generic_renaming_declaration         8.5.5
       package_body                         7.2
       package_renaming_declaration         8.5.3
       package_specification                7.1
       subprogram_specification             6.1

    delay_alternative
       select_alternative                   9.7.1
       timed_entry_call                     9.7.2

    delay_relative_statement
       delay_statement                      9.6

    delay_statement
       delay_alternative                    9.7.1
       simple_statement                     5.1
       triggering_statement                 9.7.4

    delay_until_statement
       delay_statement                      9.6

    delta_constraint
       scalar_constraint                    3.2.2

    derived_type_definition
       type_definition                      3.2.1

    designator
       subprogram_body                      6.3

    digit
       extended_digit                       2.4.2
       graphic_character                    2.1
       letter_or_digit                      2.3
       numeral                              2.4.1

    digits_constraint
       scalar_constraint                    3.2.2

    direct_name
       accept_statement                     9.5.2
       at_clause                            J.7
       local_name                           13.1
       name                                 4.1
       statement_identifier                 5.1
       variant_part                         3.8.1

    discrete_choice
       discrete_choice_list                 3.8.1

    discrete_choice_list
       array_component_association          4.3.3
       case_statement_alternative           5.4
       variant                              3.8.1

    discrete_range
       discrete_choice                      3.8.1
       index_constraint                     3.6.1
       slice                                4.1.2

    discrete_subtype_definition
       constrained_array_definition         3.6
       entry_declaration                    9.5.2
       entry_index_specification            9.5.2
       loop_parameter_specification         5.5

    discriminant_association
       discriminant_constraint              3.7.1

    discriminant_constraint
       composite_constraint                 3.2.2

    discriminant_part
       formal_type_declaration              12.5
       incomplete_type_declaration          3.10.1
       private_extension_declaration        7.3
       private_type_declaration             7.3

    discriminant_specification
       known_discriminant_part              3.7

    entry_barrier
       entry_body                           9.5.2

    entry_body
       protected_operation_item             9.4

    entry_body_formal_part
       entry_body                           9.5.2

    entry_call_alternative
       conditional_entry_call               9.7.3
       timed_entry_call                     9.7.2

    entry_call_statement
       entry_call_alternative               9.7.2
       simple_statement                     5.1
       triggering_statement                 9.7.4

    entry_declaration
       protected_operation_declaration      9.4
       task_item                            9.1

    entry_index
       accept_statement                     9.5.2

    entry_index_specification
       entry_body_formal_part               9.5.2

    enumeration_aggregate
       enumeration_representation_clause    13.4

    enumeration_literal_specification
       enumeration_type_definition          3.5.1

    enumeration_representation_clause
       representation_clause                13.1

    enumeration_type_definition
       type_definition                      3.2.1

    exception_choice
       exception_handler                    11.2

    exception_declaration
       basic_declaration                    3.1

    exception_handler
       handled_sequence_of_statements       11.2

    exception_renaming_declaration
       renaming_declaration                 8.5

    exit_statement
       simple_statement                     5.1

    explicit_actual_parameter
       parameter_association                6.4

    explicit_dereference
       name                                 4.1

    explicit_generic_actual_parameter
       generic_association                  12.3

    exponent
       based_literal                        2.4.2
       decimal_literal                      2.4.1

    expression
       ancestor_part                        4.3.2
       array_component_association          4.3.3
       assignment_statement                 5.2
       at_clause                            J.7
       attribute_definition_clause          13.3
       attribute_designator                 4.1.4
       case_statement                       5.4
       condition                            5.3
       decimal_fixed_point_definition       3.5.9
       default_expression                   3.7
       delay_relative_statement             9.6
       delay_until_statement                9.6
       delta_constraint                     J.3
       digits_constraint                    3.5.9
       discrete_choice                      3.8.1
       discriminant_association             3.7.1
       entry_index                          9.5.2
       explicit_actual_parameter            6.4
       explicit_generic_actual_parameter    12.3
       floating_point_definition            3.5.7
       indexed_component                    4.1.1
       mod_clause                           J.8
       modular_type_definition              3.5.4
       number_declaration                   3.3.2
       object_declaration                   3.3.1
       ordinary_fixed_point_definition      3.5.9
       position                             13.5.1
       positional_array_aggregate           4.3.3
       pragma_argument_association          2.8
       primary                              4.4
       qualified_expression                 4.7
       range_attribute_designator           4.1.4
       record_component_association         4.3.1
       restriction                          13.12
       return_statement                     6.5
       type_conversion                      4.6

    extended_digit
       based_numeral                        2.4.2

    extension_aggregate
       aggregate                            4.3

    factor
       term                                 4.4

    first_bit
       component_clause                     13.5.1

    fixed_point_definition
       real_type_definition                 3.5.6

    floating_point_definition
       real_type_definition                 3.5.6

    formal_access_type_definition
       formal_type_definition               12.5

    formal_array_type_definition
       formal_type_definition               12.5

    formal_decimal_fixed_point_definition
       formal_type_definition               12.5

    formal_derived_type_definition
       formal_type_definition               12.5

    formal_discrete_type_definition
       formal_type_definition               12.5

    formal_floating_point_definition
       formal_type_definition               12.5

    formal_modular_type_definition
       formal_type_definition               12.5

    formal_object_declaration
       generic_formal_parameter_declaration 12.1

    formal_ordinary_fixed_point_definition
       formal_type_definition               12.5

    formal_package_actual_part
       formal_package_declaration           12.7

    formal_package_declaration
       generic_formal_parameter_declaration 12.1

    formal_part
       parameter_and_result_profile         6.1
       parameter_profile                    6.1

    formal_private_type_definition
       formal_type_definition               12.5

    formal_signed_integer_type_definition
       formal_type_definition               12.5

    formal_subprogram_declaration
       generic_formal_parameter_declaration 12.1

    formal_type_declaration
       generic_formal_parameter_declaration 12.1

    formal_type_definition
       formal_type_declaration              12.5

    format_effector
       character                            2.1

    full_type_declaration
       type_declaration                     3.2.1

    function_call
       name                                 4.1

    general_access_modifier
       access_to_object_definition          3.10

    generic_actual_part
       formal_package_actual_part           12.7
       generic_instantiation                12.3

    generic_association
       generic_actual_part                  12.3

    generic_declaration
       basic_declaration                    3.1
       library_unit_declaration             10.1.1

    generic_formal_parameter_declaration
       generic_formal_part                  12.1

    generic_formal_part
       generic_package_declaration          12.1
       generic_subprogram_declaration       12.1

    generic_instantiation
       basic_declaration                    3.1
       library_unit_declaration             10.1.1

    generic_package_declaration
       generic_declaration                  12.1

    generic_renaming_declaration
       library_unit_renaming_declaration    10.1.1
       renaming_declaration                 8.5

    generic_subprogram_declaration
       generic_declaration                  12.1

    goto_statement
       simple_statement                     5.1

    graphic_character
       character                            2.1
       character_literal                    2.5
       string_element                       2.6

    guard
       selective_accept                     9.7.1

    handled_sequence_of_statements
       accept_statement                     9.5.2
       block_statement                      5.6
       entry_body                           9.5.2
       package_body                         7.2
       subprogram_body                      6.3
       task_body                            9.1

    identifier
       accept_statement                     9.5.2
       attribute_designator                 4.1.4
       block_statement                      5.6
       defining_identifier                  3.1
       designator                           6.1
       direct_name                          4.1
       entry_body                           9.5.2
       loop_statement                       5.5
       package_body                         7.2
       package_specification                7.1
       pragma                               2.8
       pragma_argument_association          2.8
       protected_body                       9.4
       protected_definition                 9.4
       restriction                          13.12
       selector_name                        4.1.3
       task_body                            9.1
       task_definition                      9.1

    identifier_letter
       graphic_character                    2.1
       identifier                           2.3
       letter_or_digit                      2.3

    if_statement
       compound_statement                   5.1

    implicit_dereference
       prefix                               4.1

    incomplete_type_declaration
       type_declaration                     3.2.1

    index_constraint
       composite_constraint                 3.2.2

    index_subtype_definition
       unconstrained_array_definition       3.6

    indexed_component
       name                                 4.1

    integer_type_definition
       type_definition                      3.2.1

    iteration_scheme
       loop_statement                       5.5

    known_discriminant_part
       discriminant_part                    3.7
       full_type_declaration                3.2.1
       protected_type_declaration           9.4
       task_type_declaration                9.1

    label
       statement                            5.1

    last_bit
       component_clause                     13.5.1

    letter_or_digit
       identifier                           2.3

    library_item
       compilation_unit                     10.1.1

    library_unit_body
       library_item                         10.1.1

    library_unit_declaration
       library_item                         10.1.1

    library_unit_renaming_declaration
       library_item                         10.1.1

    local_name
       attribute_definition_clause          13.3
       component_clause                     13.5.1
       enumeration_representation_clause    13.4
       record_representation_clause         13.5.1

    loop_parameter_specification
       iteration_scheme                     5.5

    loop_statement
       compound_statement                   5.1

    mod_clause
       record_representation_clause         13.5.1

    mode
       formal_object_declaration            12.4
       parameter_specification              6.1

    modular_type_definition
       integer_type_definition              3.5.4

    multiplying_operator
       term                                 4.4

    name
       abort_statement                      9.8
       assignment_statement                 5.2
       attribute_definition_clause          13.3
       default_name                         12.6
       entry_call_statement                 9.5.3
       exception_choice                     11.2
       exception_renaming_declaration       8.5.2
       exit_statement                       5.7
       explicit_actual_parameter            6.4
       explicit_dereference                 4.1
       explicit_generic_actual_parameter    12.3
       formal_package_declaration           12.7
       function_call                        6.4
       generic_instantiation                12.3
       generic_renaming_declaration         8.5.5
       goto_statement                       5.8
       implicit_dereference                 4.1
       local_name                           13.1
       object_renaming_declaration          8.5.1
       package_renaming_declaration         8.5.3
       parent_unit_name                     10.1.1
       pragma_argument_association          2.8
       prefix                               4.1
       primary                              4.4
       procedure_call_statement             6.4
       raise_statement                      11.3
       requeue_statement                    9.5.4
       subprogram_renaming_declaration      8.5.4
       subtype_mark                         3.2.2
       type_conversion                      4.6
       use_package_clause                   8.4
       with_clause                          10.1.2

    named_array_aggregate
       array_aggregate                      4.3.3

    null_statement
       simple_statement                     5.1

    number_declaration
       basic_declaration                    3.1

    numeral
       base                                 2.4.2
       decimal_literal                      2.4.1
       exponent                             2.4.1

    numeric_literal
       primary                              4.4

    object_declaration
       basic_declaration                    3.1

    object_renaming_declaration
       renaming_declaration                 8.5

    operator_symbol
       defining_operator_symbol             6.1
       designator                           6.1
       direct_name                          4.1
       selector_name                        4.1.3

    ordinary_fixed_point_definition
       fixed_point_definition               3.5.9

    other_control_function
       character                            2.1

    package_body
       library_unit_body                    10.1.1
       proper_body                          3.11

    package_body_stub
       body_stub                            10.1.3

    package_declaration
       basic_declaration                    3.1
       library_unit_declaration             10.1.1

    package_renaming_declaration
       library_unit_renaming_declaration    10.1.1
       renaming_declaration                 8.5

    package_specification
       generic_package_declaration          12.1
       package_declaration                  7.1

    parameter_and_result_profile
       access_to_subprogram_definition      3.10
       subprogram_specification             6.1

    parameter_association
       actual_parameter_part                6.4

    parameter_profile
       accept_statement                     9.5.2
       access_to_subprogram_definition      3.10
       entry_body_formal_part               9.5.2
       entry_declaration                    9.5.2
       subprogram_specification             6.1

    parameter_specification
       formal_part                          6.1

    parent_unit_name
       defining_program_unit_name           6.1
       designator                           6.1
       package_body                         7.2
       package_specification                7.1
       subunit                              10.1.3

    position
       component_clause                     13.5.1

    positional_array_aggregate
       array_aggregate                      4.3.3

    pragma_argument_association
       pragma                               2.8

    prefix
       attribute_reference                  4.1.4
       function_call                        6.4
       indexed_component                    4.1.1
       procedure_call_statement             6.4
       range_attribute_reference            4.1.4
       selected_component                   4.1.3
       slice                                4.1.2

    primary
       factor                               4.4

    private_extension_declaration
       type_declaration                     3.2.1

    private_type_declaration
       type_declaration                     3.2.1

    procedure_call_statement
       simple_statement                     5.1

    proper_body
       body                                 3.11
       subunit                              10.1.3

    protected_body
       proper_body                          3.11

    protected_body_stub
       body_stub                            10.1.3

    protected_definition
       protected_type_declaration           9.4
       single_protected_declaration         9.4

    protected_element_declaration
       protected_definition                 9.4

    protected_operation_declaration
       protected_definition                 9.4
       protected_element_declaration        9.4

    protected_operation_item
       protected_body                       9.4

    protected_type_declaration
       full_type_declaration                3.2.1

    qualified_expression
       allocator                            4.8
       code_statement                       13.8
       primary                              4.4

    raise_statement
       simple_statement                     5.1

    range
       discrete_range                       3.6.1
       discrete_subtype_definition          3.6
       range_constraint                     3.5
       relation                             4.4

    range_attribute_designator
       range_attribute_reference            4.1.4

    range_attribute_reference
       range                                3.5

    range_constraint
       delta_constraint                     J.3
       digits_constraint                    3.5.9
       scalar_constraint                    3.2.2

    real_range_specification
       decimal_fixed_point_definition       3.5.9
       floating_point_definition            3.5.7
       ordinary_fixed_point_definition      3.5.9

    real_type_definition
       type_definition                      3.2.1

    record_aggregate
       aggregate                            4.3

    record_component_association
       record_component_association_list    4.3.1

    record_component_association_list
       extension_aggregate                  4.3.2
       record_aggregate                     4.3.1

    record_definition
       record_extension_part                3.9.1
       record_type_definition               3.8

    record_extension_part
       derived_type_definition              3.4

    record_representation_clause
       representation_clause                13.1

    record_type_definition
       type_definition                      3.2.1

    relation
       expression                           4.4

    relational_operator
       relation                             4.4

    renaming_declaration
       basic_declaration                    3.1

    representation_clause
       basic_declarative_item               3.11
       component_item                       3.8
       protected_operation_declaration      9.4
       protected_operation_item             9.4
       task_item                            9.1

    requeue_statement
       simple_statement                     5.1

    return_statement
       simple_statement                     5.1

    scalar_constraint
       constraint                           3.2.2

    select_alternative
       selective_accept                     9.7.1

    select_statement
       compound_statement                   5.1

    selected_component
       name                                 4.1

    selective_accept
       select_statement                     9.7

    selector_name
       component_choice_list                4.3.1
       discriminant_association             3.7.1
       generic_association                  12.3
       parameter_association                6.4
       selected_component                   4.1.3

    sequence_of_statements
       abortable_part                       9.7.4
       accept_alternative                   9.7.1
       case_statement_alternative           5.4
       conditional_entry_call               9.7.3
       delay_alternative                    9.7.1
       entry_call_alternative               9.7.2
       exception_handler                    11.2
       handled_sequence_of_statements       11.2
       if_statement                         5.3
       loop_statement                       5.5
       selective_accept                     9.7.1
       triggering_alternative               9.7.4

    signed_integer_type_definition
       integer_type_definition              3.5.4

    simple_expression
       first_bit                            13.5.1
       last_bit                             13.5.1
       range                                3.5
       real_range_specification             3.5.7
       relation                             4.4
       signed_integer_type_definition       3.5.4

    simple_statement
       statement                            5.1

    single_protected_declaration
       object_declaration                   3.3.1

    single_task_declaration
       object_declaration                   3.3.1

    slice
       name                                 4.1

    space_character
       graphic_character                    2.1

    special_character
       graphic_character                    2.1

    statement
       sequence_of_statements               5.1

    statement_identifier
       block_statement                      5.6
       label                                5.1
       loop_statement                       5.5

    string_element
       string_literal                       2.6

    string_literal
       operator_symbol                      6.1
       primary                              4.4

    subprogram_body
       library_unit_body                    10.1.1
       proper_body                          3.11
       protected_operation_item             9.4

    subprogram_body_stub
       body_stub                            10.1.3

    subprogram_declaration
       basic_declaration                    3.1
       library_unit_declaration             10.1.1
       protected_operation_declaration      9.4
       protected_operation_item             9.4

    subprogram_default
       formal_subprogram_declaration        12.6

    subprogram_renaming_declaration
       library_unit_renaming_declaration    10.1.1
       renaming_declaration                 8.5

    subprogram_specification
       abstract_subprogram_declaration      6.1
       formal_subprogram_declaration        12.6
       generic_subprogram_declaration       12.1
       subprogram_body                      6.3
       subprogram_body_stub                 10.1.3
       subprogram_declaration               6.1
       subprogram_renaming_declaration      8.5.4

    subtype_declaration
       basic_declaration                    3.1

    subtype_indication
       access_to_object_definition          3.10
       allocator                            4.8
       component_definition                 3.6
       derived_type_definition              3.4
       discrete_range                       3.6.1
       discrete_subtype_definition          3.6
       object_declaration                   3.3.1
       private_extension_declaration        7.3
       subtype_declaration                  3.2.2

    subtype_mark
       access_definition                    3.10
       ancestor_part                        4.3.2
       discriminant_specification           3.7
       explicit_generic_actual_parameter    12.3
       formal_derived_type_definition       12.5.1
       formal_object_declaration            12.4
       index_subtype_definition             3.6
       object_renaming_declaration          8.5.1
       parameter_and_result_profile         6.1
       parameter_specification              6.1
       qualified_expression                 4.7
       relation                             4.4
       subtype_indication                   3.2.2
       type_conversion                      4.6
       use_type_clause                      8.4

    subunit
       compilation_unit                     10.1.1

    task_body
       proper_body                          3.11

    task_body_stub
       body_stub                            10.1.3

    task_definition
       single_task_declaration              9.1
       task_type_declaration                9.1

    task_item
       task_definition                      9.1

    task_type_declaration
       full_type_declaration                3.2.1

    term
       simple_expression                    4.4

    terminate_alternative
       select_alternative                   9.7.1

    timed_entry_call
       select_statement                     9.7

    triggering_alternative
       asynchronous_select                  9.7.4

    triggering_statement
       triggering_alternative               9.7.4

    type_conversion
       name                                 4.1

    type_declaration
       basic_declaration                    3.1

    type_definition
       full_type_declaration                3.2.1

    unary_adding_operator
       simple_expression                    4.4

    unconstrained_array_definition
       array_type_definition                3.6

    underline
       based_numeral                        2.4.2
       identifier                           2.3
       numeral                              2.4.1

    unknown_discriminant_part
       discriminant_part                    3.7

    use_clause
       basic_declarative_item               3.11
       context_item                         10.1.2
       generic_formal_part                  12.1

    use_package_clause
       use_clause                           8.4

    use_type_clause
       use_clause                           8.4

    variant
       variant_part                         3.8.1

    variant_part
       component_list                       3.8

    with_clause
       context_item                         10.1.2
Index


Index entries are given by paragraph number.  A list of all language-defined
library units may be found under Language-Defined Library Units.  A list of
all language-defined types may be found under Language-Defined Types.



& operator   4.4(1), 4.5.3(3)

* operator   4.4(1), 4.5.5(1)
** operator   4.4(1), 4.5.6(7)

+ operator   4.4(1), 4.5.3(1), 4.5.4(1)

= operator   4.4(1), 4.5.2(1)

- operator   4.4(1), 4.5.3(1), 4.5.4(1)

/ operator   4.4(1), 4.5.5(1)
/= operator   4.4(1), 4.5.2(1)

< operator   4.4(1), 4.5.2(1)
<= operator   4.4(1), 4.5.2(1)

> operator   4.4(1), 4.5.2(1)
>= operator   4.4(1), 4.5.2(1)

10646-1:1993, ISO/IEC standard   1.2(8)
1539:1991, ISO/IEC standard   1.2(3)
1989:1985, ISO standard   1.2(4)

6429:1992, ISO/IEC standard   1.2(5)
646:1991, ISO/IEC standard   1.2(2)

8859-1:1987, ISO/IEC standard   1.2(6)

9899:1990, ISO/IEC standard   1.2(7)

A   6.3.1(21), 7.3(7), 7.3.1(7), 8.6(34), 9.5.2(13), 10.1.1(12), 10.1.2(8),
        10.2(27), 12.3(22), 13.1(7), 13.14(19)
A.B   10.1.2(8)
A.B.C   10.1.2(8)
A.B.C.D   10.1.2(8)
A.B.X   10.1.2(8)
A.B.Y   10.1.2(8)
A_Form   4.6(66)
A_View   6.3.1(21)
A0   3.10.2(22)
A1   3.10.2(22), 13.1(14), 13.14(13)
A2   13.1(14), 13.14(13)
A3   13.14(13)
abnormal completion   7.6.1(2)
abnormal state of an object   13.9.1(4)
   [partial]   9.8(21), 11.6(6), A.13(17)
abnormal task   9.8(4)
abnormal termination
   of a partition   10.2(25)
abort
   of a partition   E.1(7)
   of a task   9.8(4)
   of the execution of a construct   9.8(5)
abort completion point   9.8(15)
abort-deferred operation   9.8(5)
abort_statement   9.8(2)
   used   5.1(4), P(1)
Abort_Task   C.7.1(3)
abortable_part   9.7.4(5)
   used   9.7.4(2), P(1)
abs operator   4.4(1), 4.5.6(1)
absolute value   4.4(1), 4.5.6(1)
abstract data type (ADT)
   See also abstract type   3.9.3(1)
   See private types and private extensions   7.3(1)
abstract subprogram   3.9.3(1), 3.9.3(3)
abstract type   3.9.3(1), 3.9.3(2)
abstract_subprogram_declaration   6.1(3)
   used   3.1(3), P(1)
Acc   13.11(42)
accept_alternative   9.7.1(5)
   used   9.7.1(4), P(1)
accept_statement   9.5.2(3)
   used   5.1(5), 9.7.1(5), P(1)
acceptable interpretation   8.6(14)
Access attribute   3.10.2(24), 3.10.2(32), K(2), K(4)
   See also Unchecked_Access attribute   13.10(3)
access discriminant   3.7(9)
access parameter   6.1(24)
access paths
   distinct   6.2(12)
Access type   3.2(2), 3.10(1), N(2)
access types
   input-output unspecified   A.7(6)
access value   3.10(1)
access-to-constant type   3.10(10)
access-to-object type   3.10(7)
access-to-subprogram type   3.10(7), 3.10(11)
access-to-variable type   3.10(10)
Access_Check   11.5(11)
   [partial]   4.1(13), 4.6(49)
access_definition   3.10(6)
   used   3.7(5), 6.1(15), P(1)
Access_State   A.5.2(27)
access_type_definition   3.10(2)
   used   3.2.1(4), 12.5.4(2), P(1)
access_to_object_definition   3.10(3)
   used   3.10(2), P(1)
access_to_subprogram_definition   3.10(5)
   used   3.10(2), P(1)
accessibility
   from shared passive library units   E.2.1(8)
accessibility level   3.10.2(3)
accessibility rule
   Access attribute   3.10.2(28), 3.10.2(32)
   checking in generic units   12.3(11)
   not part of generic contract   3.9.1(4)
   record extension   3.9.1(3)
   requeue statement   9.5.4(6)
   type conversion   4.6(17), 4.6(20)
Accessibility_Check   11.5(21)
   [partial]   3.10.2(29), 4.6(48), 6.5(17), E.4(18)
accessible partition   E.1(7)
accuracy   4.6(32), G.2(1)
ACID   1.3(1)
ACK   A.3.3(5), J.5(4)
acquire
   execution resource associated with protected object   9.5.1(5)
Activate   6.4(19)
activation
   of a task   9.2(1)
activation failure   9.2(1)
activator
   of a task   9.2(5)
active partition   10.2(28), E.1(2)
active priority   D.1(15)
actual   12.3(7), 12.3(18)
actual duration   D.9(12)
actual parameter
   for a formal parameter   6.4.1(3)
actual subtype   3.3(23), 12.5(4)
   of an object   3.3.1(9)
actual type   12.5(4)
actual_parameter_part   6.4(4)
   used   6.4(2), 6.4(3), 9.5.3(2), P(1)
Acute   A.3.3(22)
ACVC
   Ada Compiler Validation Capability   1.1.2(37)
Ada   A.2(2)
Ada calling convention   6.3.1(3)
Ada Commentary Integration Document (ACID)   1.3(1)
Ada Compiler Validation Capability
   ACVC   1.1.2(37)
Ada Issue (AI)   1.3(1)
Ada Rapporteur Group (ARG)   1.3(1)
Ada.Asynchronous_Task_Control   D.11(3)
Ada.Calendar   9.6(10)
Ada.Characters   A.3.1(2)
Ada.Characters.Handling   A.3.2(2)
Ada.Characters.Latin_1   A.3.3(3)
Ada.Command_Line   A.15(3)
Ada.Decimal   F.2(2)
Ada.Direct_IO   A.8.4(2)
Ada.Dynamic_Priorities   D.5(3)
Ada.Exceptions   11.4.1(2)
Ada.Finalization   7.6(4)
Ada.Float_Text_IO   A.10.9(33)
Ada.Float_Wide_Text_IO   A.11(3)
Ada.Integer_Text_IO   A.10.8(21)
Ada.Integer_Wide_Text_IO   A.11(3)
Ada.Interrupts   C.3.2(2)
Ada.Interrupts.Names   C.3.2(12)
Ada.Numerics   A.5(3)
Ada.Numerics.Complex_Elementary_Functions   G.1.2(9)
Ada.Numerics.Complex_Types   G.1.1(25)
Ada.Numerics.Discrete_Random   A.5.2(17)
Ada.Numerics.Elementary_Functions   A.5.1(9)
Ada.Numerics.Float_Random   A.5.2(5)
Ada.Numerics.Generic_Complex_Elementary_Functions   G.1.2(2)
Ada.Numerics.Generic_Complex_Types   G.1.1(2)
Ada.Numerics.Generic_Elementary_Functions   A.5.1(3)
Ada.Real_Time   D.8(3)
Ada.Sequential_IO   A.8.1(2)
Ada.Storage_IO   A.9(3)
Ada.Streams   13.13.1(2)
Ada.Streams.Stream_IO   A.12.1(3)
Ada.Strings   A.4.1(3)
Ada.Strings.Bounded   A.4.4(3)
Ada.Strings.Fixed   A.4.3(5)
Ada.Strings.Maps   A.4.2(3)
Ada.Strings.Maps.Constants   A.4.6(3)
Ada.Strings.Unbounded   A.4.5(3)
Ada.Strings.Wide_Bounded   A.4.7(1)
Ada.Strings.Wide_Fixed   A.4.7(1)
Ada.Strings.Wide_Maps   A.4.7(3)
Ada.Strings.Wide_Maps.Wide_Constants   A.4.7(1)
Ada.Strings.Wide_Unbounded   A.4.7(1)
Ada.Synchronous_Task_Control   D.10(3)
Ada.Tags   3.9(6)
Ada.Task_Attributes   C.7.2(2)
Ada.Task_Identification   C.7.1(2)
Ada.Text_IO   A.10.1(2)
Ada.Text_IO.Complex_IO   G.1.3(3)
Ada.Text_IO.Editing   F.3.3(3)
Ada.Text_IO.Text_Streams   A.12.2(3)
Ada.Unchecked_Conversion   13.9(3)
Ada.Unchecked_Deallocation   13.11.2(3)
Ada.Wide_Text_IO   A.11(2)
Ada.Wide_Text_IO.Complex_IO   G.1.4(1)
Ada.Wide_Text_IO.Editing   F.3.4(1)
Ada.Wide_Text_IO.Text_Streams   A.12.3(3)
Ada.IO_Exceptions   A.13(3)
Ada_Application   B.5(29)
Ada_Employee_Record_Type   B.4(118)
Add   10.1.1(35)
Addition   3.9.1(16)
Address   13.7(12)
   arithmetic   13.7.1(6)
   comparison   13.7(14)
   null   13.7(12)
Address attribute   13.3(11), J.7.1(5), K(6)
Address clause   13.3(7), 13.3(12)
Address_To_Access_Conversions
   child of System   13.7.2(2)
Adjacent attribute   A.5.3(48), K(8)
Adjust   7.6(2), 7.6(6)
adjusting the value of an object   7.6(15), 7.6(16)
adjustment   7.6(15), 7.6(16)
   as part of assignment   5.2(14)
Adjustments_Conversions   B.4(121)
Adjustments_Type   B.4(114)
ADT (abstract data type)
   See also abstract type   3.9.3(1)
   See private types and private extensions   7.3(1)
advice   1.1.2(37)
Aft attribute   3.5.10(5), K(12)
aggregate   4.3(1), 4.3(2)
   used   4.4(7), 4.7(2), P(1)
   See also composite type   3.2(2)
AI   1.3(1)
aliased   3.10(9), N(3)
aliasing
   See distinct access paths   6.2(12)
Alignment   A.4.1(6)
Alignment attribute   13.3(23), K(14)
Alignment clause   13.3(7), 13.3(25)
All_Calls_Remote pragma   E.2.3(5), L(2)
All_Checks   11.5(25)
Allocate   13.11(7)
allocator   4.8(2)
   used   4.4(7), P(1)
Alphanumeric   B.4(16)
alphanumeric character
   a category of Character   A.3.2(31)
Alphanumeric_Set   A.4.6(4)
ambiguous   8.6(30)
ambiguous grammar   1.1.4(14)
ampersand   2.1(15), A.3.3(8)
ampersand operator   4.4(1), 4.5.3(3)
ancestor   3.9.3(6), 12.3(18)
   of a library unit   10.1.1(11)
   of a type   3.4.1(10)
   ultimate   3.4.1(10)
ancestor subtype
   of a private_extension_declaration   7.3(8)
   of a formal derived type   12.5.1(5)
ancestor_part   4.3.2(3)
   used   4.3.2(2), P(1)
and operator   4.4(1), 4.5.1(2)
and then (short-circuit control form)   4.4(1), 4.5.1(1)
Angle   12.5(13)
angle threshold   G.2.4(10)
Annex
   informative   1.1.2(18)
   normative   1.1.2(14)
   Specialized Needs   1.1.2(7)
anonymous access type   3.10(12)
anonymous array type   3.3.1(1)
anonymous protected type   3.3.1(1)
anonymous task type   3.3.1(1)
anonymous type   3.2.1(7)
Another_Int   7.3.1(7)
Any_Priority   13.7(16), D.1(10)
APC   A.3.3(19)
apostrophe   2.1(15), A.3.3(8)
Append   A.4.4(13), A.4.4(14), A.4.4(15), A.4.4(16), A.4.4(17), A.4.4(18),
        A.4.4(19), A.4.4(20), A.4.5(12), A.4.5(13), A.4.5(14)
Append_All   10.1.1(35)
Append_Image   10.1.1(35)
applicable index constraint   4.3.3(10)
application areas   1.1.2(7)
apply
   to a loop_statement by an exit_statement   5.7(4)
   to a callable construct by a return_statement   6.5(4)
   to a program unit by a program unit pragma   10.1.5(2)
arbitrary order   1.1.4(18)
Arccos   A.5.1(6), G.1.2(5)
Arccosh   A.5.1(7), G.1.2(7)
Arccot   A.5.1(6), G.1.2(5)
Arccoth   A.5.1(7), G.1.2(7)
Arcsin   A.5.1(6), G.1.2(5)
Arcsinh   A.5.1(7), G.1.2(7)
Arctan   A.5.1(6), G.1.2(5)
Arctanh   A.5.1(7), G.1.2(7)
ARG   1.3(1)
Argument   A.15(5), G.1.1(10)
argument of a pragma   2.8(9)
Argument_Count   A.15(4)
Argument_Error   A.5(3)
array   3.6(1)
array component expression   4.3.3(6)
array indexing
   See indexed_component   4.1.1(1)
array slice   4.1.2(1)
Array type   3.2(2), 3.6(1), N(4)
array_aggregate   4.3.3(2)
   used   4.3(2), 13.4(3), P(1)
array_component_association   4.3.3(5)
   used   4.3.3(4), P(1)
array_type_definition   3.6(2)
   used   3.2.1(4), 3.3.1(2), 12.5.3(2), P(1)
Array1   13.1(14)
Array2   13.1(14)
ASCII   A.1(36), J.5(2)
   package physically nested within the declaration of Standard   A.1(36)
aspect of representation   13.1(8)
   coding   13.4(7)
   controlled   13.11.3(5)
   convention, calling convention   B.1(28)
   exported   B.1(28)
   imported   B.1(28)
   layout   13.5(1)
   packing   13.2(5)
   record layout   13.5(1)
   specifiable attributes   13.3(5)
   storage place   13.5(1)
assembly language   C.1(4)
assign   7.6(17)
   See assignment operation   5.2(3)
assigning back of parameters   6.4.1(17)
assignment
   user-defined   7.6(1)
assignment operation   5.2(3), 5.2(12), 7.6(13)
   during elaboration of an object_declaration   3.3.1(19)
   during evaluation of a generic_association for a formal object of mode in
        12.4(11)
   during evaluation of a parameter_association   6.4.1(11)
   during evaluation of an aggregate   4.3(5)
   during evaluation of an initialized allocator   4.8(7)
   during evaluation of an uninitialized allocator   4.8(9), 4.8(10)
   during evaluation of concatenation   4.5.3(10)
   during execution of a for loop   5.5(9)
   during execution of a return_statement   6.5(21)
   during execution of an assignment_statement   5.2(12)
   during parameter copy back   6.4.1(17)
   list of uses   7.6.1(24)
assignment_statement   5.2(2)
   used   5.1(4), P(1)
associated components
   of a record_component_association   4.3.1(10)
associated discriminants
   of a named discriminant_association   3.7.1(5)
   of a positional discriminant_association   3.7.1(5)
associated object
   of a value of a by-reference type   6.2(10)
   of a value of a limited type   6.2(10)
asterisk   2.1(15), A.3.3(8)
asynchronous
   remote procedure call   E.4.1(9)
Asynchronous pragma   E.4.1(3), L(3)
asynchronous remote procedure call   E.4(1)
asynchronous_select   9.7.4(2)
   used   9.7(2), P(1)
Asynchronous_Task_Control
   child of Ada   D.11(3)
at-most-once execution   E.4(11)
at_clause   J.7(1)
   used   13.1(2), P(1)
atomic   C.6(7)
Atomic pragma   C.6(3), L(4)
Atomic_Components pragma   C.6(5), L(5)
Attach_Handler   C.3.2(7)
Attach_Handler pragma   C.3.1(4), L(6)
attaching
   to an interrupt   C.3(2)
attribute   4.1.4(1), C.7.2(2), K(1)
   representation   13.3(1)
   specifiable   13.3(5)
   specifying   13.3(1)
attribute_definition_clause   13.3(2)
   used   13.1(2), P(1)
attribute_designator   4.1.4(3)
   used   4.1.4(2), 13.1(3), 13.3(2), P(1)
Attribute_Handle   C.7.2(3)
attribute_reference   4.1.4(2)
   used   4.1(2), P(1)
attributes
   Access   3.10.2(24), 3.10.2(32), K(2), K(4)
   Address   13.3(11), J.7.1(5), K(6)
   Adjacent   A.5.3(48), K(8)
   Aft   3.5.10(5), K(12)
   Alignment   13.3(23), K(14)
   Base   3.5(15), K(17)
   Bit_Order   13.5.3(4), K(19)
   Body_Version   E.3(4), K(21)
   Callable   9.9(2), K(23)
   Caller   C.7.1(14), K(25)
   Ceiling   A.5.3(33), K(27)
   Class   3.9(14), 7.3.1(9), K(31), K(34)
   Component_Size   13.3(69), K(36)
   Compose   A.5.3(24), K(38)
   Constrained   3.7.2(3), J.4(2), K(42)
   Copy_Sign   A.5.3(51), K(44)
   Count   9.9(5), K(48)
   Definite   12.5.1(23), K(50)
   Delta   3.5.10(3), K(52)
   Denorm   A.5.3(9), K(54)
   Digits   3.5.8(2), 3.5.10(7), K(56), K(58)
   Exponent   A.5.3(18), K(60)
   External_Tag   13.3(75), K(64)
   First   3.5(12), 3.6.2(3), K(68), K(70)
   First(N)   3.6.2(4), K(66)
   First_Bit   13.5.2(3), K(72)
   Floor   A.5.3(30), K(74)
   Fore   3.5.10(4), K(78)
   Fraction   A.5.3(21), K(80)
   Identity   11.4.1(9), C.7.1(12), K(84), K(86)
   Image   3.5(35), K(88)
   Input   13.13.2(22), 13.13.2(32), K(92), K(96)
   Last   3.5(13), 3.6.2(5), K(102), K(104)
   Last(N)   3.6.2(6), K(100)
   Last_Bit   13.5.2(4), K(106)
   Leading_Part   A.5.3(54), K(108)
   Length   3.6.2(9), K(117)
   Length(N)   3.6.2(10), K(115)
   Machine   A.5.3(60), K(119)
   Machine_Emax   A.5.3(8), K(123)
   Machine_Emin   A.5.3(7), K(125)
   Machine_Mantissa   A.5.3(6), K(127)
   Machine_Overflows   A.5.3(12), A.5.4(4), K(129), K(131)
   Machine_Radix   A.5.3(2), A.5.4(2), K(133), K(135)
   Machine_Rounds   A.5.3(11), A.5.4(3), K(137), K(139)
   Max   3.5(19), K(141)
   Max_Size_In_Storage_Elements   13.11.1(3), K(145)
   Min   3.5(16), K(147)
   Model   A.5.3(68), G.2.2(7), K(151)
   Model_Emin   A.5.3(65), G.2.2(4), K(155)
   Model_Epsilon   A.5.3(66), K(157)
   Model_Mantissa   A.5.3(64), G.2.2(3), K(159)
   Model_Small   A.5.3(67), K(161)
   Modulus   3.5.4(17), K(163)
   Output   13.13.2(19), 13.13.2(29), K(165), K(169)
   Partition_ID   E.1(9), K(173)
   Pos   3.5.5(2), K(175)
   Position   13.5.2(2), K(179)
   Pred   3.5(25), K(181)
   Range   3.5(14), 3.6.2(7), K(187), K(189)
   Range(N)   3.6.2(8), K(185)
   Read   13.13.2(6), 13.13.2(14), K(191), K(195)
   Remainder   A.5.3(45), K(199)
   Round   3.5.10(12), K(203)
   Rounding   A.5.3(36), K(207)
   Safe_First   A.5.3(71), G.2.2(5), K(211)
   Safe_Last   A.5.3(72), G.2.2(6), K(213)
   Scale   3.5.10(11), K(215)
   Scaling   A.5.3(27), K(217)
   Signed_Zeros   A.5.3(13), K(221)
   Size   13.3(40), 13.3(45), K(223), K(228)
   Small   3.5.10(2), K(230)
   Storage_Pool   13.11(13), K(232)
   Storage_Size   13.3(60), 13.11(14), J.9(2), K(234), K(236)
   Succ   3.5(22), K(238)
   Tag   3.9(16), 3.9(18), K(242), K(244)
   Terminated   9.9(3), K(246)
   Truncation   A.5.3(42), K(248)
   Unbiased_Rounding   A.5.3(39), K(252)
   Unchecked_Access   13.10(3), H.4(18), K(256)
   Val   3.5.5(5), K(258)
   Valid   13.9.2(3), H(6), K(262)
   Value   3.5(52), K(264)
   Version   E.3(3), K(268)
   Wide_Image   3.5(28), K(270)
   Wide_Value   3.5(40), K(274)
   Wide_Width   3.5(38), K(278)
   Width   3.5(39), K(280)
   Write   13.13.2(3), 13.13.2(11), K(282), K(286)
avoid overspecifying environmental issues   10(3)

B   6.3.1(21), 10.1.1(12), 10.2(27), 12.3(22)
Backus-Naur Form (BNF)
   complete listing   P(1)
   cross reference   P(1)
   notation   1.1.4(3)
   under Syntax heading   1.1.2(25)
Bad   4.9(44), 12.3(11)
Bag   10.1.1(35)
Bag_Image   10.1.1(35)
Bags_Of_My_Type   10.1.1(35)
base   2.4.2(3), 2.4.2(6)
base 16 literal   2.4.2(1)
   used   2.4.2(2), P(1)
base 2 literal   2.4.2(1)
base 8 literal   2.4.2(1)
Base attribute   3.5(15), K(17)
base decimal precision
   of a floating point type   3.5.7(9), 3.5.7(10)
base priority   D.1(15)
base range
   of a decimal fixed point type   3.5.9(16)
   of a fixed point type   3.5.9(12)
   of a floating point type   3.5.7(8), 3.5.7(10)
   of a modular type   3.5.4(10)
   of a scalar type   3.5(6)
   of a signed integer type   3.5.4(9)
   of an enumeration type   3.5(6)
   of an ordinary fixed point type   3.5.9(13)
base subtype
   of a type   3.5(15)
based_literal   2.4.2(2)
   used   2.4(2), P(1)
based_numeral   2.4.2(4)
   used   2.4.2(2), P(1)
basic letter
   a category of Character   A.3.2(27)
basic_declaration   3.1(3)
   used   3.11(4), P(1)
basic_declarative_item   3.11(4)
   used   3.11(3), 7.1(3), P(1)
Basic_Map   A.4.6(5)
Basic_Set   A.4.6(4)
Beaujolais effect   8.4(1)
   [partial]   3.6(18), 8.6(22), 8.6(34)
become nonlimited   7.3.1(5), 7.5(16)
BEL   A.3.3(5)
belong
   to a range   3.5(4)
   to a subtype   3.2(8)
Bias   12.2(10)
bibliography   1.2(1)
Big   13.3(48)
big endian   13.5.3(2)
binary   B.4(10)
   literal   2.4.2(1)
binary adding operator   4.5.3(1)
binary literal   2.4.2(1)
binary operator   4.5(9)
binary_adding_operator   4.5(4)
   used   4.4(4), P(1)
Binary_Format   B.4(24)
Binary_Operation   3.9.1(15)
Binop_Ptr   3.10(22)
bit field
   See record_representation_clause   13.5.1(1)
bit ordering   13.5.3(2)
bit string
   See logical operators on boolean arrays   4.5.1(2)
Bit_Order   13.7(15)
Bit_Order attribute   13.5.3(4), K(19)
Bit_Order clause   13.3(7), 13.5.3(4)
Bit_Vector   3.6(26)
blank
   in text input for enumeration and numeric types   A.10.6(5)
block_statement   5.6(2)
   used   5.1(5), P(1)
blocked
   [partial]   D.2.1(11)
   a task state   9(10)
   during an entry call   9.5.3(19)
   execution of a selective_accept   9.7.1(16)
   on a delay_statement   9.6(21)
   on an accept_statement   9.5.2(24)
   waiting for activations to complete   9.2(5)
   waiting for dependents to terminate   9.3(5)
blocked interrupt   C.3(2)
blocking, potentially   9.5.1(8)
   Abort_Task   C.7.1(16)
   delay_statement   9.6(34), D.9(5)
   remote subprogram call   E.4(17)
   RPC operations   E.5(23)
   Suspend_Until_True   D.10(10)
BMP   3.5.2(2), 3.5.2(3)
BNF (Backus-Naur Form)
   complete listing   P(1)
   cross reference   P(1)
   notation   1.1.4(3)
   under Syntax heading   1.1.2(25)
body   3.11(5)
   used   3.11(3), P(1)
body_stub   10.1.3(2)
   used   3.11(5), P(1)
Body_Version attribute   E.3(4), K(21)
Boolean   3.5.3(1), A.1(5)
boolean type   3.5.3(1)
Bounded
   child of Ada.Strings   A.4.4(3)
bounded error   1.1.2(31), 1.1.5(8), 6.2(12), 7.6.1(14), 9.5.1(8), 9.8(20),
        10.2(26), 13.9.1(9), 13.11.2(11), C.7.1(17), D.5(11), E.1(10),
        E.3(6), J.7.1(11)
Bounded_String   A.4.4(6), A.4.4(106)
Bounded_String_Internals   A.4.4(106)
bounds
   of a discrete_range   3.6.1(6)
   of an array   3.6(13)
   of the index range of an array_aggregate   4.3.3(24)
box
   compound delimiter   3.6(15)
broadcast signal
   See protected object   9.4(1)
   See requeue   9.5.4(1)
Broken_Bar   A.3.3(21)
BS   A.3.3(5), J.5(4)
Buffer   3.7(33), 9.11(8), 9.11(9), 12.5(12)
Buffer_Size   3.5.4(35), A.9(4)
Buffer_Type   A.9(4)
by copy parameter passing   6.2(2)
by reference parameter passing   6.2(2)
by-copy type   6.2(3)
by-reference type   6.2(4)
   atomic or volatile   C.6(18)
Byte   3.5.4(36), 13.3(80), B.4(29)
   See storage element   13.3(8)
byte sex
   See ordering of storage elements in a word   13.5.3(5)
Byte_Array   B.4(29)
Byte_Mask   13.5.1(27)

C   3.6(11), 4.3.3(42), 10.1.1(12), 10.2(27), B.3(77), B.3.2(46)
   child of Interfaces   B.3(4)
C interface   B.3(1)
C standard   1.2(7)
C_float   B.3(15)
Calendar   J.1(8)
   child of Ada   9.6(10)
call   6(2)
call on a dispatching operation   3.9.2(2)
callable   9.9(2)
Callable attribute   9.9(2), K(23)
callable construct   6(2)
callable entity   6(2)
called partition   E.4(1)
Caller attribute   C.7.1(14), K(25)
calling convention   6.3.1(2), B.1(11)
   Ada   6.3.1(3)
   associated with a designated profile   3.10(11)
   entry   6.3.1(13)
   Intrinsic   6.3.1(4)
   protected   6.3.1(12)
calling partition   E.4(1)
calling stub   E.4(10)
CAN   A.3.3(6), J.5(4)
cancellation
   of a delay_statement   9.6(22)
   of an entry call   9.5.3(20)
cancellation of a remote subprogram call   E.4(13)
canonical form   A.5.3(3)
canonical semantics   11.6(2)
canonical-form representation   A.5.3(10)
Car   3.10.1(19), 3.10.1(21), 12.5.4(10), 12.5.4(11)
Car_Name   3.10.1(20), 12.5.4(10)
case insensitive   2.3(5)
case_statement   5.4(2)
   used   5.1(5), P(1)
case_statement_alternative   5.4(3)
   used   5.4(2), P(1)
cast
   See type conversion   4.6(1)
   See unchecked type conversion   13.9(1)
catch (an exception)
   See handle   11(1)
categorization pragma   E.2(2)
   Remote_Call_Interface   E.2.3(2)
   Remote_Types   E.2.2(2)
   Shared_Passive   E.2.1(2)
categorized library unit   E.2(2)
catenation operator
   See concatenation operator   4.4(1), 4.5.3(3)
CCH   A.3.3(18)
Cedilla   A.3.3(22)
Ceiling attribute   A.5.3(33), K(27)
ceiling priority
   of a protected object   D.3(8)
Ceiling_Check
   [partial]   C.3.1(11), D.3(13)
Cell   3.10.1(15), 3.10.1(16)
Cent_Sign   A.3.3(21)
change of representation   13.6(1)
Changes by comment number
   [94-3786.a]   E.2(9), E.2(12), E.2(13), E.2.2(4), E.2.2(7), E.2.2(8),
        E.2.3(7), E.2.3(14)
   [94-4409.a]   7.2(4)
   [94-4426.a]   9.1(9), 9.4(11)
   [94-4438.a]   B.2(10)
   [94-4439.a]   7.3.1(7)
   [94-4443.a]   7.3(7)
   [94-4444.a]   7.3.1(7)
   [94-4445.a]   13.7.1(13)
   [94-4448.a]   3.5.7(8)
   [94-4450.a]   3.2.3(7)
   [94-4451.a]   3.2.3(7)
   [94-4453.a]   3.2.3(7)
   [94-4455.a]   G.2.2(11)
   [94-4457.a]   3.9.2(20), 3.9.2(21)
   [94-4460.a]   10.2(19)
   [94-4461.a]   10.2(19)
   [94-4465.a]   A.4.7(27)
   [94-4469.a]   A.3.2(19), A.4.6(1), A.4.6(6), A.4.7(1), A.4.7(28),
        A.4.7(29)
   [94-4471.a]   A.4.3(42)
   [94-4472.a]   E(1)
   [94-4472.d]   E.1(15)
   [94-4472.f]   E.1(5)
   [94-4472.g]   E.1(6)
   [94-4472.i]   E.1(11)
   [94-4472.l]   E.2(4)
   [94-4472.n]   E.2.1(5)
   [94-4472.q]   E.2.3(15)
   [94-4472.r]   E.2.3(19)
   [94-4472.s]   E.3(1)
   [94-4472.v]   E.4(7)
   [94-4472.z]   E.4(18)
   [94-4472.za]   E.4(18)
   [94-4472.zb]   E.4(20)
   [94-4472.zc]   E.4(20)
   [94-4472.zf]   E.4(20)
   [94-4472.zj]   E.5(23)
   [94-4472.zk]   E.5(28)
   [94-4474.a]   7.3(11), 12.5.1(15)
   [94-4477.a]   6.3.2(6)
   [94-4480.f]   F.3.3(16), F.3.3(45)
   [94-4481.a]   4.5(10), 4.5.2(11), 4.6(32)
   [94-4485.d]   1.1.3(7)
   [94-4485.f]   1.2(8)
   [94-4487.a]   A.1(47)
   [94-4488.a]   A.3.3(26)
   [94-4491.a]   B.3(41), B.3(52), B.3(59)
   [94-4493.c]   4.1.3(7), 7.3(9), 13.5.2(1)
   [94-4493.d]   2.9(3)
   [94-4495.a]   7.6(19)
   [94-4497.a]   A.4.2(63)
   [94-4498.b]   A.4.3(91)
   [94-4500.a]   8.5.1(3), 12.4(5)
   [94-4501.a]   11.5(28)
   [94-4502.a]   3.5.9(18)
   [94-4505.a]   8.5.1(3), 12.4(5)
   [94-4506.a]   8.5.1(3), 12.4(5)
   [94-4507.a]   8.5.1(3), 12.4(5)
   [94-4509.a]   8.5.1(3), 12.4(5)
   [94-4510.a]   A.1(47)
   [94-4514.a]   3.9.1(10)
   [94-4523.a]   E.5(21)
   [94-4526.a]   A.10.9(36)
   [94-4526.b]   3.5(33), 3.5(51), A.10.9(20), A.10.9(23)
   [94-4526.c]   3.5(56), A.10.9(35)
   [94-4526.d]   A.10.8(8)
   [94-4526.e]   A.10.9(18)
   [94-4527.a]   A.10.1(19), A.10.3(4), A.10.3(6)
   [94-4528.a]   7.6(4), 13.9(3), A.4.5(72)
   [94-4532.a]   8.5.1(3), 12.4(5)
   [94-4535.a]   3.4(38)
   [94-4535.c]   3.4(26)
   [94-4535.d]   3.4(12)
   [94-4537.b]   3.4(12)
   [94-4539.a]   4.9(26)
   [94-4539.b]   4.1.4(12)
   [94-4539.c]   4.5.2(11), 4.9(38), 13.1(7)
   [94-4540.a]   E.5(21)
   [94-4541.a]   E.5(21)
   [94-4542.a]   E.5(21)
   [94-4553.a]   E.5(12), E.5(21)
   [94-4556.a]   11.4.2(10)
   [94-4560.a]   5.7(1)
   [94-4561.a]   11.4.2(10)
   [94-4567.a]   D.7(18)
   [94-4570.a]   3.10.2(1)
   [94-4571.a]   B.3(41), B.3(52), B.3(59)
   [94-4572.a]   6.2(12)
   [94-4572.b]   6.2(12)
   [94-4572.c]   6.2(12)
   [94-4573.a]   6.2(12)
   [94-4574.c]   G.1.4(1)
   [94-4577.a]   10.2(19)
   [94-4587.a]   A.5.3(64), A.5.3(65), A.5.3(70)
   [94-4599.a]   10(2)
   [94-4599.c]   10.2(19)
   [94-4599.f]   10.1(3), N(22)
   [94-4603.a]   4.3.3(1)
   [94-4605.a]   5.7(1)
   [94-4606.a]   A.4.2(26), A.4.2(37), A.4.2(58), A.4.5(72), A.4.7(27)
   [94-4610.a]   3.7(26)
   [94-4618.a]   3.10.1(7)
   [94-4619.a]   7.6(9)
   [94-4625.a]   10.1.1(22), 10.1.1(27), 10.1.2(8)
   [94-4626.a]   10.1.1(22), 10.1.1(27), 10.1.2(8)
   [94-4630.e]   A.5.3(32)
   [94-4630.f]   A.5.3(35)
   [94-4657.a]   E.2(9), E.2(12), E.2(13), E.2.2(4), E.2.2(7), E.2.2(8),
        E.2.3(7), E.2.3(14)
   [94-4658.a]   E.2(9), E.2(12), E.2(13), E.2.2(4), E.2.2(7), E.2.2(8),
        E.2.3(7), E.2.3(14)
   [94-4661.a]   D.1(11)
   [94-4662.a]   7.3(6)
   [94-4663.a]   3.8(10)
   [94-4664.a]   3.8(10)
   [94-4665.a]   7.3(6)
   [94-4666.a]   8.3(28)
   [94-4666.b]   8.4(8)
   [94-4666.c]   8.5.4(10)
   [94-4667.c]   4.3.3(42)
   [94-4667.f]   4.5.2(17)
   [94-4667.l]   4.6(28)
   [94-4667.p]   4.9(10)
   [94-4672.a]   E.2(9), E.2(12), E.2(13), E.2.2(4), E.2.2(7), E.2.2(8),
        E.2.3(7), E.2.3(14)
   [94-4673.a]   E.2.1(11)
   [94-4674.a]   E.2(9), E.2(12), E.2(13), E.2.2(4), E.2.2(7), E.2.2(8),
        E.2.3(7), E.2.3(14)
   [94-4677.a]   7.3.1(7)
   [94-4678.a]   7.3.1(6)
   [94-4679.a]   4.9(1), 4.9(2), 4.9(20)
   [94-4679.c]   4.9(7)
   [94-4682.a]   7.3.1(7)
   [94-4683.a]   7.3.1(6)
   [94-4684.a]   4.9(1), 4.9(2), 4.9(20)
   [94-4684.c]   4.9(7)
   [94-4687.a]   4.9(1), 4.9(2), 4.9(20)
   [94-4692.a]   3.10.2(32), 4.6(20)
   [94-4693.i]   A.1(51)
   [94-4693.o]   K(1)
   [94-4693.p]   L(1)
   [94-4693.q]   M(1)
   [94-4693.r]   N(1)
   [94-4693.s]   P(1)
   [94-4693.v]   3.5.5(10), 3.5.8(3), 4.5.6(7), A.1(19)
   [94-4697.a]   B.3(41), B.3(48), B.3(56), B.3.1(21), B.3.1(23)
   [94-4701.a]   6.6(6)
   [94-4702.a]   3.10.2(32), 4.6(20)
   [94-4704.a]   A.1(47)
   [94-4706.a]   3.10.2(32), 4.6(20)
   [94-4708.a]   3.10.2(32), 4.6(20)
   [94-4709.a]   A.1(47), A.3.3(26)
   [94-4712.a]   1.1.3(4)
   [94-4715.a]   3.7(27), 3.7.1(9), 3.9.1(3), 3.10.2(1), 3.10.2(28),
        3.10.2(29), 3.10.2(32), 4.6(17), 4.6(20), 4.6(48), 6.5(19), 7.6.1(1),
        7.6.1(3), 7.6.1(4), 9.3(3), 9.3(7), 9.5.4(6), 9.8(13), 9.8(20),
        11.5(21)
   [94-4718.c]   6.3.1(21), 6.3.1(25)
   [94-4723.a]   E.2(9), E.2(12), E.2(13), E.2.2(4), E.2.2(7), E.2.2(8),
        E.2.3(7), E.2.3(14)
   [94-4724.a]   3.10.2(1)
   [94-4725.a]   3.10.2(1)
   [94-4726.a]   A.3.3(26)
   [94-4728.a]   A.4.7(27)
   [94-4737.a]   B.3(41), B.3(52), B.3(59)
   [94-4737.b]   A.5.3(8)
   [94-4738.a]   4.9(2), 4.9(20)
   [94-4745.a]   3.10.2(9)
   [94-4746.]   3.10.2(3)
   [94-4747.b]   4.9(24)
   [94-4748.b]   4.9(24)
   [94-4749.a]   1.1.3(7)
   [94-4751.a]   6.2(12)
   [94-4751.b]   6.2(12)
   [94-4751.c]   6.2(12)
   [94-4752.a]   6.3.1(21)
   [94-4753.a]   10.2(19)
   [94-4754.b]   4.9(24)
   [94-4757.a]   A.12.1(27)
   [94-4758.a]   A.15(10)
   [94-4759.a]   4.8(4)
   [94-4761.d]   2.8(27)
   [94-4761.o]   A.13(15)
   [94-4761.q]   C.3(24)
   [94-4761.u]   D.5(17)
   [94-4761.zb]   J.7.1(23)
   [94-4765.a]   J.7.1(23)
   [94-4768.b]   10.1.3(8)
   [94-4768.c]   A.8.5(4)
   [94-4768.e]   5.4(13), 13.9.1(9)
   [94-4768.h]   E.4.1(9)
   [94-4768.k]   3.5.10(7)
   [94-4768.l]   C.3(21)
   [94-4768.n]   13.3(24)
   [94-4768.q]   A.4.3(91)
   [94-4768.r]   G.2.3(23)
   [94-4768.s]   A.4.7(46)
   [94-4768.t]   D.5(11)
   [94-4768.u]   13.13.2(33), K(94)
   [94-4768.v]   E.2.1(11)
   [94-4769.a]   E.2.1(11)
   [94-4770.a]   A.12.1(27)
   [94-4771.a]   11.2(11)
   [94-4774.a]   3.9(25), 6.2(10)
   [94-4774.b]   3.9.2(10), 3.10.2(32), 6.3.1(8), 6.3.1(11), 6.3.1(17),
        8.5.4(5), 12.3(11), 13.3(6)
   [94-4774.c]   8.4(16)
   [94-4774.d]   11.4.1(12)
   [94-4774.e]   G.2.3(27)
   [94-4774.f]   J.3(3), J.3(7)
   [94-4776.a]   1.1.5(6)
   [94-4776.b]   3.5.4(23)
   [94-4776.c]   4.9(32)
   [94-4776.d]   9.5.3(19)
   [94-4776.e]   13.3(49)
   [94-4776.f]   13.5.1(8)
   [94-4776.g]   13.7(36)
   [94-4777.a]   12.5.1(10), 12.5.1(11)
   [94-4780.a]   3.10.2(1)
   [94-4783.a]   6.4.1(14)
   [94-4783.b]   6.4.1(14)
   [94-4784.a]   E(8), E.1(15)
   [94-4785.a]   6.4.1(14)
   [94-4786.a]   E.2.3(6)
   [94-4787.a]   E.2.3(6)
   [94-4788.b]   E(8), E.1(15)
   [94-4788.c]   E.2.3(6)
   [94-4789.a]   3.5.4(23)
   [94-4790.a]   3.5.4(23)
   [94-4791.a]   13.11.2(16)
   [94-4796.a]   13.9.1(9)
   [94-4799.a]   3.3(23), 3.3.1(22), 3.7(28)
   [94-4801.a]   3.7(28)
   [94-4804.a]   12.3(11)
   [94-4805.b]   B.3.1(28)
   [94-4806.a]   3.7(28)
   [94-4807.b]   B.3.1(28)
   [94-4808.a]   12.3(11)
   [94-4809.b]   B.3(62)
   [94-4810.a]   13.13.2(2), 13.13.2(13), 13.13.2(16), 13.13.2(18),
        13.13.2(25), 13.13.2(36)
   [94-4811.a]   A.4.5(72)
   [94-4814.a]   3.9.2(20), 3.9.2(21)
   [94-4815.a]   B.3(41)
   [94-4816.a]   B.2(4)
   [94-4817.a]   A.12(1), A.12.3(5)
   [94-4818.a]   A.4.7(27)
   [94-4819.a]   A.12.1(27)
   [94-4822.a]   13.3(24)
   [94-4824.a]   E.2(9), E.2(12), E.2(13), E.2.2(4), E.2.2(7), E.2.2(8),
        E.2.3(7), E.2.3(14)
   [94-4825.a]   13.3(24)
   [94-4827.a]   F.1(1)
   [94-4827.b]   F.1(1)
   [94-4828.b]   7.3(6)
   [94-4828.c]   9.5.4(6)
   [94-4828.d]   11.4.1(12)
   [94-4833.a]   3.9.3(6)
   [94-4834.a]   3.9.3(6)
   [94-4835.a]   13.3(24)
   [94-4842.a]   3.9(25)
   [94-4843.a]   7.6(9)
   [94-4843.b]   13.9.1(9)
   [94-4845.a]   A.7(1), A.8(2), A.8.2(5), A.8.2(8), A.8.2(14), A.8.2(17),
        A.8.2(22), A.8.2(25), A.8.2(29)
   [94-4846.a]   E(8)
   [94-4846.b]   E.2(5)
   [94-4846.d]   J.7.1(23)
   [94-4852.a]   A.4.3(91)
   [94-4855.a]   13.13.2(9), 13.13.2(17), 13.13.2(37)
   [94-4856.a]   13.2(8), 13.3(48), 13.3(52), 13.3(55)
   [94-4857.a]   3.10.2(4), 3.10.2(20), 3.10.2(22)
   [94-4857.b]   3.10.2(21)
   [94-4858.a]   3.3.1(9), 3.6(11), 3.7(11), 3.10(9)
   [94-4859.c]   H.4(27)
   [94-4860.a]   13.2(8), 13.3(48), 13.3(52), 13.3(55)
   [94-4863.a]   13.2(8), 13.3(48), 13.3(52), 13.3(55)
   [94-4873.a]   9.1(9), 9.4(11)
   [94-4874.a]   3.7(28)
   [94-4876.a]   A.4.3(91)
   [94-4878.a]   G.2.2(11)
   [94-4881.a]   9.1(9), 9.4(11)
   [94-4882.a]   3.7(28)
   [94-4883.a]   A.4.3(91)
   [94-4884.a]   A.3.2(19), A.4.5(72), A.4.6(1)
   [94-4885.a]   13.2(8), 13.3(48), 13.3(52), 13.3(55)
   [94-4886.a]   7.3(11), 7.3(12)
   [94-4887.a]   E.2.3(19)
   [94-4889.a]   G.2.2(11)
   [94-4889.c]   A.5.3(8)
   [94-4889.e]   3.5.7(8)
   [94-4889.h]   A.5.3(64), A.5.3(65), A.5.3(70)
   [94-4889.i]   G.1.4(1)
   [94-4889.k]   G.2.3(27)
   [94-4889.l]   G.2.3(23)
   [94-4889.m]   A.5.3(32), A.5.3(35)
   [94-4889.q]   B.2(10)
   [94-4890.a]   E(7)
   [94-4893.a]   13.11.2(3)
   [94-4893.b]   13.2(8), 13.3(48), 13.3(52), 13.3(55)
   [94-4893.c]   G.2.2(11)
   [94-4893.d]   3.5(56), A.10.9(35)
   [94-4894.a]   C.5(5), C.5(7)
   [94-4898.b]   H.3.1(21)
   [94-4900.a]   G.2.2(11)
   [94-4901.a]   3.5(56), A.10.9(35)
   [94-4902.a]   C.5(7)
   [94-4904.a]   C.5(7)
   [94-4905.a]   C.5(7)
   [94-4906.a]   C.5(7)
   [94-4908.a]   10.2(29)
   [94-4909.a]   13.3(24)
   [94-4910.a]   10.2.1(23)
   [94-4912.a]   11.4.1(19)
   [94-4913.a]   A.3.2(42)
   [94-4913.b]   A.4.7(27)
   [94-4913.c]   A.10.10(11)
   [94-4913.d]   B.3(41), B.3(52), B.3(59)
   [94-4913.f]   3.5.7(10), 3.5.8(2)
   [94-4918.a]   3.10.2(4), 3.10.2(20), 3.10.2(22)
   [94-4920.a]   G.2.3(18)
   [94-4921.a]   13.7.1(15), 13.7.2(6)
   [94-4926.a]   4.9(2), 4.9(37)
   [94-4927.a]   3.10.2(21)
   [94-4929.a]   4.9(2), 4.9(37)
   [94-4932.a]   A.10.9(25)
   [94-4933.a]   8.3(20), 10.1.1(19), 10.1.1(35), 10.1.2(9), 10.1.6(2),
        12.2(2)
   [94-4934.a]   G.2.2(11)
   [94-4935.a]   3.5.7(10), 3.5.8(2)
   [94-4936.a]   3.9.3(3)
   [94-4941.a]   7.3(7)
   [94-4942.a]   8.3(18), 8.3(29)
   [94-4944.a]   10.1.1(19)
   [94-4946.a]   7.3(7)
   [94-4947.a]   7.3(12)
   [94-4949.a]   3.9.3(3)
   [94-4950.a]   4.9(2), 4.9(37)
   [94-4952.a]   G.2.3(22)
   [94-4954.a]   13.9(15)
   [94-4965.a]   B.3.2(23)
   [94-4966.a]   13.9(15)
   [94-4967.a]   D.2.1(9), D.2.2(18)
   [94-4968.a]   4.9(8)
   [94-4969.a]   13.13.2(38)
   [94-4970.a]   A.4.2(66)
   [94-4971.a]   A.4.4(1), A.4.5(1)
   [94-4972.a]   A.10.3(4), A.10.3(6)
   [94-4973.a]   10.1.5(2)
   [94-4974.a]   F.3.1(43)
   [94-4975.a]   A.10.3(19)
   [94-4976.a]   A.15(10)
   [94-4977.a]   J.5(9)
   [94-4978.a]   3.10(9), 3.10.2(24)
   [94-4979.a]   F.3.2(57)
   [94-4979.b]   F.3.2(56)
   [94-4980.a]   B.4(50), B.4(72)
   [94-4981.a]   B.3.2(16)
   [94-4982.a]   A.3.3(26)
   [94-4983.a]   A.5.3(32)
   [94-4983.b]   A.5.3(35)
   [94-4983.c]   G.2(1)
   [94-4984.a]   A.15(20)
   [94-4985.a]   F.3.1(42)
   [94-4985.b]   F.3.2(10), F.3.2(19)
   [94-4985.c]   F.3.3(17)
   [94-4985.d]   F.3.2(16)
   [94-4985.e]   F.3.1(38), F.3.2(64), F.3.2(67), F.3.2(70)
   [94-4985.f]   F.3.2(4)
   [94-5000.g]   11.4.2(10)
   [94-5001.b]   3.9.2(20)
   [94-5001.d]   4.9(40)
   [94-5001.g]   7.3(7)
   [94-5001.h]   8.5.1(3)
   [94-5001.i]   11.4.2(10)
   [94-5001.k]   13.1(14)
   [94-5002.a]   10.1.1(28)
   [94-5005.c]   4.9(40)
   [95-9999.a]   1(2)
Changes by paragraph number
   1(2)   [95-9999.a]
   1.1.3(4)   [94-4712.a]
   1.1.3(7)   [94-4485.d], [94-4749.a]
   1.1.5(6)   [94-4776.a]
   1.2(8)   [94-4485.f]
   10(2)   [94-4599.a]
   10.1(3)   [94-4599.f]
   10.1.1(19)   [94-4933.a], [94-4944.a]
   10.1.1(22)   [94-4625.a], [94-4626.a]
   10.1.1(27)   [94-4625.a], [94-4626.a]
   10.1.1(28)   [94-5002.a]
   10.1.1(35)   [94-4933.a]
   10.1.2(8)   [94-4625.a], [94-4626.a]
   10.1.2(9)   [94-4933.a]
   10.1.3(8)   [94-4768.b]
   10.1.5(2)   [94-4973.a]
   10.1.6(2)   [94-4933.a]
   10.2(19)   [94-4599.c], [94-4577.a], [94-4460.a], [94-4461.a], [94-4753.a]
   10.2(29)   [94-4908.a]
   10.2.1(23)   [94-4910.a]
   11.2(11)   [94-4771.a]
   11.4.1(12)   [94-4774.d], [94-4828.d]
   11.4.1(19)   [94-4912.a]
   11.4.2(10)   [94-4556.a], [94-4561.a], [94-5000.g], [94-5001.i]
   11.5(21)   [94-4715.a]
   11.5(28)   [94-4501.a]
   12.2(2)   [94-4933.a]
   12.3(11)   [94-4804.a], [94-4808.a], [94-4774.b]
   12.4(5)   [94-4500.a], [94-4505.a], [94-4506.a], [94-4507.a], [94-4509.a],
        [94-4532.a]
   12.5.1(10)   [94-4777.a]
   12.5.1(11)   [94-4777.a]
   12.5.1(15)   [94-4474.a]
   13.1(14)   [94-5001.k]
   13.1(7)   [94-4539.c]
   13.11.2(16)   [94-4791.a]
   13.11.2(3)   [94-4893.a]
   13.13.2(13)   [94-4810.a]
   13.13.2(16)   [94-4810.a]
   13.13.2(17)   [94-4855.a]
   13.13.2(18)   [94-4810.a]
   13.13.2(2)   [94-4810.a]
   13.13.2(25)   [94-4810.a]
   13.13.2(33)   [94-4768.u]
   13.13.2(36)   [94-4810.a]
   13.13.2(37)   [94-4855.a]
   13.13.2(38)   [94-4969.a]
   13.13.2(9)   [94-4855.a]
   13.2(8)   [94-4856.a], [94-4860.a], [94-4863.a], [94-4885.a], [94-4893.b]
   13.3(24)   [94-4768.n], [94-4822.a], [94-4825.a], [94-4835.a], [94-4909.a]
   13.3(48)   [94-4856.a], [94-4860.a], [94-4863.a], [94-4885.a], [94-4893.b]
   13.3(49)   [94-4776.e]
   13.3(52)   [94-4856.a], [94-4860.a], [94-4863.a], [94-4885.a], [94-4893.b]
   13.3(55)   [94-4856.a], [94-4860.a], [94-4863.a], [94-4885.a], [94-4893.b]
   13.3(6)   [94-4774.b]
   13.5.1(8)   [94-4776.f]
   13.5.2(1)   [94-4493.c]
   13.7(36)   [94-4776.g]
   13.7.1(13)   [94-4445.a]
   13.7.1(15)   [94-4921.a]
   13.7.2(6)   [94-4921.a]
   13.9(15)   [94-4954.a], [94-4966.a]
   13.9(3)   [94-4528.a]
   13.9.1(9)   [94-4796.a], [94-4768.e], [94-4843.b]
   2.8(27)   [94-4761.d]
   2.9(3)   [94-4493.d]
   3.10(9)   [94-4978.a], [94-4858.a]
   3.10.1(7)   [94-4618.a]
   3.10.2(1)   [94-4715.a], [94-4570.a], [94-4724.a], [94-4725.a],
        [94-4780.a]
   3.10.2(20)   [94-4857.a], [94-4918.a]
   3.10.2(21)   [94-4857.b], [94-4927.a]
   3.10.2(22)   [94-4857.a], [94-4918.a]
   3.10.2(24)   [94-4978.a]
   3.10.2(28)   [94-4715.a]
   3.10.2(29)   [94-4715.a]
   3.10.2(3)   [94-4746.]
   3.10.2(32)   [94-4715.a], [94-4774.b], [94-4692.a], [94-4702.a],
        [94-4706.a], [94-4708.a]
   3.10.2(4)   [94-4857.a], [94-4918.a]
   3.10.2(9)   [94-4745.a]
   3.2.3(7)   [94-4450.a], [94-4451.a], [94-4453.a]
   3.3(23)   [94-4799.a]
   3.3.1(22)   [94-4799.a]
   3.3.1(9)   [94-4858.a]
   3.4(12)   [94-4535.d], [94-4537.b]
   3.4(26)   [94-4535.c]
   3.4(38)   [94-4535.a]
   3.5(33)   [94-4526.b]
   3.5(51)   [94-4526.b]
   3.5(56)   [94-4526.c], [94-4893.d], [94-4901.a]
   3.5.10(7)   [94-4768.k]
   3.5.4(23)   [94-4776.b], [94-4789.a], [94-4790.a]
   3.5.5(10)   [94-4693.v]
   3.5.7(10)   [94-4935.a], [94-4913.f]
   3.5.7(8)   [94-4448.a], [94-4889.e]
   3.5.8(2)   [94-4935.a], [94-4913.f]
   3.5.8(3)   [94-4693.v]
   3.5.9(18)   [94-4502.a]
   3.6(11)   [94-4858.a]
   3.7(11)   [94-4858.a]
   3.7(26)   [94-4610.a]
   3.7(27)   [94-4715.a]
   3.7(28)   [94-4799.a], [94-4801.a], [94-4806.a], [94-4874.a], [94-4882.a]
   3.7.1(9)   [94-4715.a]
   3.8(10)   [94-4663.a], [94-4664.a]
   3.9(25)   [94-4774.a], [94-4842.a]
   3.9.1(10)   [94-4514.a]
   3.9.1(3)   [94-4715.a]
   3.9.2(10)   [94-4774.b]
   3.9.2(20)   [94-5001.b], [94-4457.a], [94-4814.a]
   3.9.2(21)   [94-4457.a], [94-4814.a]
   3.9.3(3)   [94-4936.a], [94-4949.a]
   3.9.3(6)   [94-4833.a], [94-4834.a]
   4.1.3(7)   [94-4493.c]
   4.1.4(12)   [94-4539.b]
   4.3.3(1)   [94-4603.a]
   4.3.3(42)   [94-4667.c]
   4.5(10)   [94-4481.a]
   4.5.2(11)   [94-4481.a], [94-4539.c]
   4.5.2(17)   [94-4667.f]
   4.5.6(7)   [94-4693.v]
   4.6(17)   [94-4715.a]
   4.6(20)   [94-4715.a], [94-4692.a], [94-4702.a], [94-4706.a], [94-4708.a]
   4.6(28)   [94-4667.l]
   4.6(32)   [94-4481.a]
   4.6(48)   [94-4715.a]
   4.8(4)   [94-4759.a]
   4.9(1)   [94-4679.a], [94-4684.a], [94-4687.a]
   4.9(10)   [94-4667.p]
   4.9(2)   [94-4679.a], [94-4684.a], [94-4687.a], [94-4738.a], [94-4926.a],
        [94-4929.a], [94-4950.a]
   4.9(20)   [94-4679.a], [94-4684.a], [94-4687.a], [94-4738.a]
   4.9(24)   [94-4747.b], [94-4748.b], [94-4754.b]
   4.9(26)   [94-4539.a]
   4.9(32)   [94-4776.c]
   4.9(37)   [94-4926.a], [94-4929.a], [94-4950.a]
   4.9(38)   [94-4539.c]
   4.9(40)   [94-5001.d], [94-5005.c]
   4.9(7)   [94-4679.c], [94-4684.c]
   4.9(8)   [94-4968.a]
   5.4(13)   [94-4768.e]
   5.7(1)   [94-4605.a], [94-4560.a]
   6.2(10)   [94-4774.a]
   6.2(12)   [94-4573.a], [94-4572.a], [94-4751.a], [94-4572.b], [94-4751.b],
        [94-4572.c], [94-4751.c]
   6.3.1(11)   [94-4774.b]
   6.3.1(17)   [94-4774.b]
   6.3.1(21)   [94-4718.c], [94-4752.a]
   6.3.1(25)   [94-4718.c]
   6.3.1(8)   [94-4774.b]
   6.3.2(6)   [94-4477.a]
   6.4.1(14)   [94-4783.a], [94-4785.a], [94-4783.b]
   6.5(19)   [94-4715.a]
   6.6(6)   [94-4701.a]
   7.2(4)   [94-4409.a]
   7.3(11)   [94-4474.a], [94-4886.a]
   7.3(12)   [94-4886.a], [94-4947.a]
   7.3(6)   [94-4662.a], [94-4665.a], [94-4828.b]
   7.3(7)   [94-4443.a], [94-4941.a], [94-4946.a], [94-5001.g]
   7.3(9)   [94-4493.c]
   7.3.1(6)   [94-4678.a], [94-4683.a]
   7.3.1(7)   [94-4677.a], [94-4682.a], [94-4439.a], [94-4444.a]
   7.6(19)   [94-4495.a]
   7.6(4)   [94-4528.a]
   7.6(9)   [94-4619.a], [94-4843.a]
   7.6.1(1)   [94-4715.a]
   7.6.1(3)   [94-4715.a]
   7.6.1(4)   [94-4715.a]
   8.3(18)   [94-4942.a]
   8.3(20)   [94-4933.a]
   8.3(28)   [94-4666.a]
   8.3(29)   [94-4942.a]
   8.4(16)   [94-4774.c]
   8.4(8)   [94-4666.b]
   8.5.1(3)   [94-4500.a], [94-4505.a], [94-4506.a], [94-4507.a],
        [94-4509.a], [94-4532.a], [94-5001.h]
   8.5.4(10)   [94-4666.c]
   8.5.4(5)   [94-4774.b]
   9.1(9)   [94-4426.a], [94-4873.a], [94-4881.a]
   9.3(3)   [94-4715.a]
   9.3(7)   [94-4715.a]
   9.4(11)   [94-4426.a], [94-4873.a], [94-4881.a]
   9.5.3(19)   [94-4776.d]
   9.5.4(6)   [94-4715.a], [94-4828.c]
   9.8(13)   [94-4715.a]
   9.8(20)   [94-4715.a]
   A.1(19)   [94-4693.v]
   A.1(47)   [94-4487.a], [94-4704.a], [94-4510.a], [94-4709.a]
   A.1(51)   [94-4693.i]
   A.10.1(19)   [94-4527.a]
   A.10.10(11)   [94-4913.c]
   A.10.3(19)   [94-4975.a]
   A.10.3(4)   [94-4527.a], [94-4972.a]
   A.10.3(6)   [94-4527.a], [94-4972.a]
   A.10.8(8)   [94-4526.d]
   A.10.9(18)   [94-4526.e]
   A.10.9(20)   [94-4526.b]
   A.10.9(23)   [94-4526.b]
   A.10.9(25)   [94-4932.a]
   A.10.9(35)   [94-4526.c], [94-4893.d], [94-4901.a]
   A.10.9(36)   [94-4526.a]
   A.12(1)   [94-4817.a]
   A.12.1(27)   [94-4757.a], [94-4770.a], [94-4819.a]
   A.12.3(5)   [94-4817.a]
   A.13(15)   [94-4761.o]
   A.15(10)   [94-4758.a], [94-4976.a]
   A.15(20)   [94-4984.a]
   A.3.2(19)   [94-4469.a], [94-4884.a]
   A.3.2(42)   [94-4913.a]
   A.3.3(26)   [94-4488.a], [94-4709.a], [94-4726.a], [94-4982.a]
   A.4.2(26)   [94-4606.a]
   A.4.2(37)   [94-4606.a]
   A.4.2(58)   [94-4606.a]
   A.4.2(63)   [94-4497.a]
   A.4.2(66)   [94-4970.a]
   A.4.3(42)   [94-4471.a]
   A.4.3(91)   [94-4498.b], [94-4768.q], [94-4852.a], [94-4876.a],
        [94-4883.a]
   A.4.4(1)   [94-4971.a]
   A.4.5(1)   [94-4971.a]
   A.4.5(72)   [94-4528.a], [94-4811.a], [94-4884.a], [94-4606.a]
   A.4.6(1)   [94-4469.a], [94-4884.a]
   A.4.6(6)   [94-4469.a]
   A.4.7(1)   [94-4469.a]
   A.4.7(27)   [94-4606.a], [94-4465.a], [94-4818.a], [94-4728.a],
        [94-4913.b]
   A.4.7(28)   [94-4469.a]
   A.4.7(29)   [94-4469.a]
   A.4.7(46)   [94-4768.s]
   A.5.3(32)   [94-4630.e], [94-4889.m], [94-4983.a]
   A.5.3(35)   [94-4630.f], [94-4889.m], [94-4983.b]
   A.5.3(64)   [94-4587.a], [94-4889.h]
   A.5.3(65)   [94-4587.a], [94-4889.h]
   A.5.3(70)   [94-4587.a], [94-4889.h]
   A.5.3(8)   [94-4737.b], [94-4889.c]
   A.7(1)   [94-4845.a]
   A.8(2)   [94-4845.a]
   A.8.2(14)   [94-4845.a]
   A.8.2(17)   [94-4845.a]
   A.8.2(22)   [94-4845.a]
   A.8.2(25)   [94-4845.a]
   A.8.2(29)   [94-4845.a]
   A.8.2(5)   [94-4845.a]
   A.8.2(8)   [94-4845.a]
   A.8.5(4)   [94-4768.c]
   B.2(10)   [94-4438.a], [94-4889.q]
   B.2(4)   [94-4816.a]
   B.3(41)   [94-4697.a], [94-4491.a], [94-4571.a], [94-4737.a], [94-4913.d],
        [94-4815.a]
   B.3(48)   [94-4697.a]
   B.3(52)   [94-4491.a], [94-4571.a], [94-4737.a], [94-4913.d]
   B.3(56)   [94-4697.a]
   B.3(59)   [94-4491.a], [94-4571.a], [94-4737.a], [94-4913.d]
   B.3(62)   [94-4809.b]
   B.3.1(21)   [94-4697.a]
   B.3.1(23)   [94-4697.a]
   B.3.1(28)   [94-4805.b], [94-4807.b]
   B.3.2(16)   [94-4981.a]
   B.3.2(23)   [94-4965.a]
   B.4(50)   [94-4980.a]
   B.4(72)   [94-4980.a]
   C.3(21)   [94-4768.l]
   C.3(24)   [94-4761.q]
   C.5(5)   [94-4894.a]
   C.5(7)   [94-4894.a], [94-4902.a], [94-4904.a], [94-4905.a], [94-4906.a]
   D.1(11)   [94-4661.a]
   D.2.1(9)   [94-4967.a]
   D.2.2(18)   [94-4967.a]
   D.5(11)   [94-4768.t]
   D.5(17)   [94-4761.u]
   D.7(18)   [94-4567.a]
   E(1)   [94-4472.a]
   E(7)   [94-4890.a]
   E(8)   [94-4784.a], [94-4788.b], [94-4846.a]
   E.1(11)   [94-4472.i]
   E.1(15)   [94-4472.d], [94-4784.a], [94-4788.b]
   E.1(5)   [94-4472.f]
   E.1(6)   [94-4472.g]
   E.2(12)   [94-4657.a], [94-4658.a], [94-4672.a], [94-4674.a], [94-4723.a],
        [94-3786.a], [94-4824.a]
   E.2(13)   [94-4657.a], [94-4658.a], [94-4672.a], [94-4674.a], [94-4723.a],
        [94-3786.a], [94-4824.a]
   E.2(4)   [94-4472.l]
   E.2(5)   [94-4846.b]
   E.2(9)   [94-4657.a], [94-4658.a], [94-4672.a], [94-4674.a], [94-4723.a],
        [94-3786.a], [94-4824.a]
   E.2.1(11)   [94-4768.v], [94-4673.a], [94-4769.a]
   E.2.1(5)   [94-4472.n]
   E.2.2(4)   [94-4657.a], [94-4658.a], [94-4672.a], [94-4674.a],
        [94-4723.a], [94-3786.a], [94-4824.a]
   E.2.2(7)   [94-4657.a], [94-4658.a], [94-4672.a], [94-4674.a],
        [94-4723.a], [94-3786.a], [94-4824.a]
   E.2.2(8)   [94-4657.a], [94-4658.a], [94-4672.a], [94-4674.a],
        [94-4723.a], [94-3786.a], [94-4824.a]
   E.2.3(14)   [94-4657.a], [94-4658.a], [94-4672.a], [94-4674.a],
        [94-4723.a], [94-3786.a], [94-4824.a]
   E.2.3(15)   [94-4472.q]
   E.2.3(19)   [94-4472.r], [94-4887.a]
   E.2.3(6)   [94-4786.a], [94-4787.a], [94-4788.c]
   E.2.3(7)   [94-4657.a], [94-4658.a], [94-4672.a], [94-4674.a],
        [94-4723.a], [94-3786.a], [94-4824.a]
   E.3(1)   [94-4472.s]
   E.4(18)   [94-4472.z], [94-4472.za]
   E.4(20)   [94-4472.zb], [94-4472.zc], [94-4472.zf]
   E.4(7)   [94-4472.v]
   E.4.1(9)   [94-4768.h]
   E.5(12)   [94-4553.a]
   E.5(21)   [94-4553.a], [94-4523.a], [94-4540.a], [94-4541.a], [94-4542.a]
   E.5(23)   [94-4472.zj]
   E.5(28)   [94-4472.zk]
   F.1(1)   [94-4827.b], [94-4827.a]
   F.3.1(38)   [94-4985.e]
   F.3.1(42)   [94-4985.a]
   F.3.1(43)   [94-4974.a]
   F.3.2(10)   [94-4985.b]
   F.3.2(16)   [94-4985.d]
   F.3.2(19)   [94-4985.b]
   F.3.2(4)   [94-4985.f]
   F.3.2(56)   [94-4979.b]
   F.3.2(57)   [94-4979.a]
   F.3.2(64)   [94-4985.e]
   F.3.2(67)   [94-4985.e]
   F.3.2(70)   [94-4985.e]
   F.3.3(16)   [94-4480.f]
   F.3.3(17)   [94-4985.c]
   F.3.3(45)   [94-4480.f]
   G.1.4(1)   [94-4574.c], [94-4889.i]
   G.2(1)   [94-4983.c]
   G.2.2(11)   [94-4934.a], [94-4878.a], [94-4455.a], [94-4889.a],
        [94-4893.c], [94-4900.a]
   G.2.3(18)   [94-4920.a]
   G.2.3(22)   [94-4952.a]
   G.2.3(23)   [94-4768.r], [94-4889.l]
   G.2.3(27)   [94-4774.e], [94-4889.k]
   H.3.1(21)   [94-4898.b]
   H.4(27)   [94-4859.c]
   J.3(3)   [94-4774.f]
   J.3(7)   [94-4774.f]
   J.5(9)   [94-4977.a]
   J.7.1(23)   [94-4761.zb], [94-4765.a], [94-4846.d]
   K(1)   [94-4693.o]
   K(94)   [94-4768.u]
   L(1)   [94-4693.p]
   M(1)   [94-4693.q]
   N(1)   [94-4693.r]
   N(22)   [94-4599.f]
   P(1)   [94-4693.s]
char   B.3(19)
char_array   B.3(23), B.3(60)
CHAR_BIT   B.3(6)
Char_Ptrs   B.3.2(46)
Char_Star   B.3.2(47)
Char_IO   A.10.10(20)
character   2.1(2), 3.5.2(2), A.1(35)
   used   2.7(2), P(1)
character set   2.1(1)
character set standard
   16-bit   1.2(8)
   7-bit   1.2(2)
   8-bit   1.2(6)
   control functions   1.2(5)
Character type   3.2(2), 3.5.2(1), N(5)
character_literal   2.5(2)
   used   3.5.1(4), 4.1(2), 4.1.3(3), P(1)
Character_Mapping   A.4.2(20)
Character_Mapping_Function   A.4.2(25)
Character_Put   6.3.2(5)
Character_Range   A.4.2(6)
Character_Ranges   A.4.2(7)
Character_Sequence   A.4.2(16)
Character_Set   A.4.2(4), A.4.7(46), B.5(11)
characteristics   7.3(15)
Characters
   child of Ada   A.3.1(2)
chars_ptr   B.3.1(5)
check
   language-defined   11.5(2), 11.6(1)
check, language-defined
   Access_Check   4.1(13), 4.6(49)
   Accessibility_Check   3.10.2(29), 4.6(48), 6.5(17), E.4(18)
   Ceiling_Check   C.3.1(11), D.3(13)
   Discriminant_Check   4.1.3(15), 4.3(6), 4.3.2(8), 4.6(43), 4.6(45),
        4.6(51), 4.6(52), 4.7(4), 4.8(10)
   Division_Check   3.5.4(20), 4.5.5(22), A.5.1(28), A.5.3(47), G.1.1(40),
        G.1.2(28), K(202)
   Elaboration_Check   3.11(9)
   Index_Check   4.1.1(7), 4.1.2(7), 4.3.3(29), 4.3.3(30), 4.5.3(8), 4.6(51),
        4.7(4), 4.8(10)
   Length_Check   4.5.1(8), 4.6(37), 4.6(52)
   Overflow_Check   3.5.4(20), 4.4(11), 5.4(13), G.2.1(11), G.2.2(7),
        G.2.3(25), G.2.4(2), G.2.6(3)
   Partition_Check   E.4(19)
   Range_Check   3.2.2(11), 3.5(24), 3.5(27), 3.5(43), 3.5(44), 3.5(51),
        3.5(55), 3.5.5(7), 3.5.9(19), 4.2(11), 4.3.3(28), 4.5.1(8), 4.5.6(6),
        4.5.6(13), 4.6(28), 4.6(38), 4.6(46), 4.6(51), 4.7(4), 13.13.2(35),
        A.5.2(39), A.5.2(40), A.5.3(26), A.5.3(29), A.5.3(50), A.5.3(53),
        A.5.3(59), A.5.3(62), K(11), K(41), K(47), K(114), K(122), K(184),
        K(220), K(241)
   Reserved_Check   C.3.1(10)
   Storage_Check   11.1(6), 13.3(67), 13.11(17), D.7(15)
   Tag_Check   3.9.2(16), 4.6(42), 4.6(52), 5.2(10), 6.5(9)
child
   of a library unit   10.1.1(1)
choice
   of an exception_handler   11.2(5)
choice parameter   11.2(9)
choice_parameter_specification   11.2(4)
   used   11.2(3), P(1)
Circumflex   A.3.3(12)
class   3.2(2), N(6)
   See also package   7(1)
   See also tag   3.9(3)
   of types   3.2(2)
Class attribute   3.9(14), 7.3.1(9), K(31), K(34)
class determined for a formal type   12.5(6)
class-wide type   3.4.1(4), 3.7(26)
cleanup
   See finalization   7.6.1(1)
clock   9.6(6), 9.6(12), D.8(7)
clock jump   D.8(32)
clock tick   D.8(23)
Close   7.5(19), 7.5(20), A.8.1(8), A.8.4(8), A.10.1(11), A.12.1(10)
close result set   G.2.3(5)
closed entry   9.5.3(5)
   of a protected object   9.5.3(7)
   of a task   9.5.3(6)
closed under derivation   3.2(1), 3.2(2), 3.4(28), N(6), N(41)
closure
   downward   3.10.2(37)
COBOL   B.4(104), B.4(113)
   child of Interfaces   B.4(7)
COBOL interface   B.4(1)
COBOL standard   1.2(4)
COBOL_Character   B.4(13)
COBOL_Employee_Record_Type   B.4(115)
COBOL_Employee_IO   B.4(116)
COBOL_Record   B.4(106)
Code   4.7(7)
code_statement   13.8(2)
   used   5.1(4), P(1)
coding
   aspect of representation   13.4(7)
Coefficient   3.5.7(20)
Coin   A.5.2(58)
Col   A.10.1(37)
colon   2.1(15), A.3.3(10), J.5(6)
Color   3.2.1(15), 3.5.1(14)
Column   3.2.1(15)
column number   A.10(9)
Column_Ptr   3.5.4(35)
comma   2.1(15), A.3.3(8)
Command_Line
   child of Ada   A.15(3)
Command_Name   A.15(6)
comment   2.7(2)
comments, instructions for submission   (59)
Commercial_At   A.3.3(10)
Communication_Error   E.5(5)
Comp   12.3(11)
Comp1   7.3.1(7)
Comp2   7.3.1(7)
comparison operator
   See relational operator   4.5.2(1)
compatibility
   composite_constraint with an access subtype   3.10(15)
   constraint with a subtype   3.2.2(12)
   delta_constraint with an ordinary fixed point subtype   J.3(9)
   digits_constraint with a decimal fixed point subtype   3.5.9(18)
   digits_constraint with a floating point subtype   J.3(10)
   discriminant constraint with a subtype   3.7.1(10)
   index constraint with a subtype   3.6.1(7)
   range with a scalar subtype   3.5(8)
   range_constraint with a scalar subtype   3.5(8)
compatible
   a type, with a convention   B.1(12)
compilation   10.1.1(2)
   separate   10.1(1)
Compilation unit   10.1(2), 10.1.1(9), N(7)
compilation units needed
   by a compilation unit   10.2(2)
   remote call interface   E.2.3(18)
   shared passive library unit   E.2.1(11)
compilation_unit   10.1.1(3)
   used   10.1.1(2), P(1)
compile-time error   1.1.2(27), 1.1.5(4)
compile-time semantics   1.1.2(28)
complete context   8.6(4)
completely defined   3.11.1(8)
completion
   abnormal   7.6.1(2)
   compile-time concept   3.11.1(1)
   normal   7.6.1(2)
   run-time concept   7.6.1(2)
completion and leaving (completed and left)   7.6.1(2)
completion legality
   entry_body   9.5.2(16)
   [partial]   3.10.1(13)
Complex   3.8(28), B.5(9), G.1.1(3)
Complex_Elementary_Functions
   child of Ada.Numerics   G.1.2(9)
Complex_Types
   child of Ada.Numerics   G.1.1(25)
Complex_IO
   child of Ada.Text_IO   G.1.3(3)
   child of Ada.Wide_Text_IO   G.1.4(1)
component   3.2(2), 9.4(31), 9.4(32)
component subtype   3.6(10)
component_choice_list   4.3.1(5)
   used   4.3.1(4), P(1)
component_clause   13.5.1(3)
   used   13.5.1(2), P(1)
component_declaration   3.8(6)
   used   3.8(5), 9.4(6), P(1)
component_definition   3.6(7)
   used   3.6(3), 3.6(5), 3.8(6), P(1)
component_item   3.8(5)
   used   3.8(4), P(1)
component_list   3.8(4)
   used   3.8(3), 3.8.1(3), P(1)
Component_Size attribute   13.3(69), K(36)
Component_Size clause   13.3(7), 13.3(70)
components
   of a record type   3.8(9)
Compose attribute   A.5.3(24), K(38)
Compose_From_Cartesian   G.1.1(8)
Compose_From_Polar   G.1.1(11)
Composite   13.14(10)
composite type   3.2(2), N(8)
composite_constraint   3.2.2(7)
   used   3.2.2(5), P(1)
compound delimiter   2.2(10)
compound_statement   5.1(5)
   used   5.1(3), P(1)
Compute   5.1(16)
concatenation operator   4.4(1), 4.5.3(3)
concrete subprogram
   See nonabstract subprogram   3.9.3(1)
concrete type
   See nonabstract type   3.9.3(1)
concurrent processing
   See task   9(1)
condition   5.3(3)
   used   5.3(2), 5.5(3), 5.7(2), 9.5.2(7), 9.7.1(3), P(1)
   See also exception   11(1)
conditional_entry_call   9.7.3(2)
   used   9.7(2), P(1)
configuration
   of the partitions of a program   E(4)
configuration pragma   10.1.5(8)
   Locking_Policy   D.3(5)
   Normalize_Scalars   H.1(4)
   Queuing_Policy   D.4(5)
   Restrictions   13.12(8)
   Reviewable   H.3.1(4)
   Suppress   11.5(5)
   Task_Dispatching_Policy   D.2.2(4)
conformance   6.3.1(1)
   of an implementation with the Standard   1.1.3(1)
   See also   full conformance, mode conformance, subtype conformance, type
        conformance
Conjugate   G.1.1(12), G.1.1(15)
Connect   13.13.2(40)
consistency
   among compilation units   10.1.4(5)
constant   3.3(13)
   See also literal   4.2(1)
   See also static   4.9(1)
   result of a function_call   6.4(12)
constant object   3.3(13)
constant view   3.3(13)
Constants
   child of Ada.Strings.Maps   A.4.6(3)
constituent
   of a construct   1.1.4(17)
constrained   3.2(9)
   object   3.3.1(9), 3.10(9), 6.4.1(16)
   subtype   3.2(9), 3.4(6), 3.5(7), 3.5.1(10), 3.5.4(9), 3.5.4(10),
        3.5.7(11), 3.5.9(13), 3.5.9(16), 3.6(15), 3.6(16), 3.7(26), 3.9(15),
        3.10(14), K(33)
Constrained attribute   3.7.2(3), J.4(2), K(42)
constrained by its initial value   3.3.1(9), 3.10(9)
   [partial]   4.8(6)
constrained_array_definition   3.6(5)
   used   3.6(2), P(1)
constraint   3.2.2(5)
   used   3.2.2(3), P(1)
   [partial]   3.2(7)
   of a first array subtype   3.6(16)
   of an object   3.3.1(9)
Constraint_Error   A.1(46)
   raised by failure of run-time check   1.1.5(12), 3.2.2(12), 3.5(24),
        3.5(27), 3.5(43), 3.5(44), 3.5(51), 3.5(55), 3.5.4(20), 3.5.5(7),
        3.5.9(19), 3.9.2(16), 4.1(13), 4.1.1(7), 4.1.2(7), 4.1.3(15),
        4.2(11), 4.3(6), 4.3.2(8), 4.3.3(31), 4.4(11), 4.5(10), 4.5(11),
        4.5(12), 4.5.1(8), 4.5.3(8), 4.5.5(22), 4.5.6(6), 4.5.6(12),
        4.5.6(13), 4.6(28), 4.6(57), 4.6(60), 4.7(4), 4.8(10), 5.2(10),
        5.4(13), 6.5(9), 11.1(4), 11.4.1(14), 11.5(10), 13.9.1(9),
        13.13.2(35), A.4.3(109), A.4.7(47), A.5.1(28), A.5.1(34), A.5.2(39),
        A.5.2(40), A.5.3(26), A.5.3(29), A.5.3(47), A.5.3(50), A.5.3(53),
        A.5.3(59), A.5.3(62), A.15(14), B.3(53), B.3(54), B.4(58), E.4(19),
        E.4(20), G.1.1(40), G.1.2(28), G.2.1(12), G.2.2(7), G.2.3(26),
        G.2.4(3), G.2.6(4), K(11), K(41), K(47), K(114), K(122), K(184),
        K(202), K(220), K(241), K(261)
Construct   1.1.4(16), N(9)
constructor
   See initialization   3.3.1(19), 7.6(1)
   See initialization expression   3.3.1(4)
   See Initialize   7.6(1)
   See initialized alligator   4.8(4)
Consumer   9.11(5), 9.11(6)
context free grammar
   complete listing   P(1)
   cross reference   P(1)
   notation   1.1.4(3)
   under Syntax heading   1.1.2(25)
context_clause   10.1.2(2)
   used   10.1.1(3), P(1)
context_item   10.1.2(3)
   used   10.1.2(2), P(1)
contiguous representation
   [partial]   13.1(7), 13.5.2(5), 13.7.1(12), 13.9(9), 13.9(17), 13.11(16),
        13.11(17)
Continue   D.11(3)
contract model of generics   12.3(1)
control character
   See also format_effector   2.1(13)
   See also other_control_function   2.1(14)
   a category of Character   A.3.2(22), A.3.3(4), A.3.3(15)
Control_Set   A.4.6(4)
Controlled   7.6(5)
   aspect of representation   13.11.3(5)
Controlled pragma   13.11.3(3), L(7)
controlled type   7.6(2), 7.6(9), N(10)
Controller   9.1(26)
controlling formal parameter   3.9.2(2)
controlling operand   3.9.2(2)
controlling result   3.9.2(2)
controlling tag
   for a call on a dispatching operation   3.9.2(1)
controlling tag value   3.9.2(14)
   for the expression in an assignment_statement   5.2(9)
convention   6.3.1(2), B.1(11)
   aspect of representation   B.1(28)
Convention pragma   B.1(7), L(8)
conversion   4.6(1), 4.6(28)
   access   4.6(13), 4.6(18), 4.6(47)
   arbitrary order   1.1.4(18)
   array   4.6(9), 4.6(36)
   composite (non-array)   4.6(21), 4.6(40)
   enumeration   4.6(21), 4.6(34)
   numeric   4.6(8), 4.6(29)
   unchecked   13.9(1)
   value   4.6(5)
   view   4.6(5)
Conversion_Error   B.4(30)
convertible   4.6(4)
   required   3.7(16), 3.7.1(9), 4.6(11), 4.6(15), 6.4.1(6)
Copy   6.2(12), E.4.2(2), E.4.2(5)
copy back of parameters   6.4.1(17)
copy parameter passing   6.2(2)
Copy_Array   B.3.2(15)
Copy_Sign attribute   A.5.3(51), K(44)
Copy_Terminated_Array   B.3.2(14)
Copyright_Sign   A.3.3(21)
core language   1.1.2(2)
corresponding constraint   3.4(6)
corresponding discriminants   3.7(18)
corresponding index
   for an array_aggregate   4.3.3(8)
corresponding subtype   3.4(18)
corresponding value
   of the target type of a conversion   4.6(28)
Cos   A.5.1(5), G.1.2(4)
Cosh   A.5.1(7), G.1.2(6)
Cot   A.5.1(5), G.1.2(4)
Coth   A.5.1(7), G.1.2(6)
Count   A.4.3(13), A.4.3(14), A.4.3(15), A.4.4(48), A.4.4(49), A.4.4(50),
        A.4.5(43), A.4.5(44), A.4.5(45), A.8.4(4), A.10(10), A.10.1(5),
        A.12.1(7)
Count attribute   9.9(5), K(48)
Counter   3.4(37)
Counter_Type   3.6(11)
cover
   a type   3.4.1(9)
   of a choice and an exception   11.2(6)
cover a value   3.8.1(1)
   by a discrete_choice_list   3.8.1(13)
   by a discrete_choice   3.8.1(9)
CPU_Identifier   7.4(14)
CR   A.3.3(5)
create   3.1(12), A.8.1(6), A.8.4(6), A.10.1(9), A.12.1(8)
creation
   of a protected object   C.3.1(10)
   of a task object   D.1(17)
   of an object   3.3(1)
critical section
   See intertask communication   9.5(1)
CSI   A.3.3(19)
Currency_Sign   A.3.3(21)
current column number   A.10(9)
current index
   of an open direct file   A.8(4)
current instance
   of a generic unit   8.6(18)
   of a type   8.6(17)
current line number   A.10(9)
current mode
   of an open file   A.7(7)
current page number   A.10(9)
current size
   of an external file   A.8(3)
Current_Error   A.10.1(17), A.10.1(20)
Current_Handler   C.3.2(6)
Current_Input   A.10.1(17), A.10.1(20)
Current_Output   A.10.1(17), A.10.1(20)
Current_State   D.10(4)
Current_Stream   13.13.2(40)
Current_Task   C.7.1(3)

D   3.5.9(18)
dangling references
   prevention via accessibility rules   3.10.2(3)
Data_Error   A.8.1(15), A.8.4(18), A.9(9), A.10.1(85), A.12.1(26), A.13(4)
Date   3.8(27)
Day   3.5.1(14), 9.6(13)
Day_Duration   9.6(11)
Day_Number   9.6(11)
DC1   A.3.3(6)
DC2   A.3.3(6), J.5(4)
DC3   A.3.3(6)
DC4   A.3.3(6), J.5(4)
DCS   A.3.3(18)
Deallocate   13.11(8)
deallocation of storage   13.11.2(1)
Decimal
   child of Ada   F.2(2)
decimal digit
   a category of Character   A.3.2(28)
decimal fixed point type   3.5.9(1), 3.5.9(6)
Decimal_Conversions   B.4(31)
Decimal_Digit_Set   A.4.6(4)
Decimal_Element   B.4(12)
decimal_fixed_point_definition   3.5.9(4)
   used   3.5.9(2), P(1)
decimal_literal   2.4.1(2)
   used   2.4(2), P(1)
Decimal_Output   F.3.3(11)
Decimal_IO   A.10.1(73)
Declaration   3.1(5), 3.1(6), N(11)
declarative region
   of a construct   8.1(1)
declarative_item   3.11(3)
   used   3.11(2), P(1)
declarative_part   3.11(2)
   used   5.6(2), 6.3(2), 7.2(2), 9.1(6), 9.5.2(5), P(1)
declare   3.1(8), 3.1(12)
declared pure   10.2.1(17)
Decrement   B.3.2(11)
deeper
   accessibility level   3.10.2(3)
   statically   3.10.2(4), 3.10.2(17)
default entry queuing policy   9.5.3(17)
default treatment   C.3(5)
Default_Bit_Order   13.7(15)
Default_Currency   F.3.3(10)
default_expression   3.7(6)
   used   3.7(5), 3.8(6), 6.1(15), 12.4(2), P(1)
Default_Fill   F.3.3(10)
Default_Message_Procedure   3.10(26)
default_name   12.6(4)
   used   12.6(3), P(1)
Default_Priority   13.7(17), D.1(11)
Default_Radix_Mark   F.3.3(10)
Default_Separator   F.3.3(10)
deferred constant   7.4(2)
deferred constant declaration   3.3.1(6), 7.4(2)
defining name   3.1(10)
defining_character_literal   3.5.1(4)
   used   3.5.1(3), P(1)
defining_designator   6.1(6)
   used   6.1(4), 12.3(2), P(1)
defining_identifier   3.1(4)
   used   3.2.1(3), 3.2.2(2), 3.3.1(3), 3.5.1(3), 3.10.1(2), 5.5(4), 6.1(7),
        7.3(2), 7.3(3), 8.5.1(2), 8.5.2(2), 9.1(2), 9.1(3), 9.1(6), 9.4(2),
        9.4(3), 9.4(7), 9.5.2(2), 9.5.2(5), 9.5.2(8), 10.1.3(4), 10.1.3(5),
        10.1.3(6), 11.2(4), 12.5(2), 12.7(2), P(1)
defining_identifier_list   3.3.1(3)
   used   3.3.1(2), 3.3.2(2), 3.7(5), 3.8(6), 6.1(15), 11.1(2), 12.4(2), P(1)
defining_operator_symbol   6.1(11)
   used   6.1(6), P(1)
defining_program_unit_name   6.1(7)
   used   6.1(4), 6.1(6), 7.1(3), 7.2(2), 8.5.3(2), 8.5.5(2), 12.3(2), P(1)
Definite attribute   12.5.1(23), K(50)
definite subtype   3.3(23)
Definition   3.1(7), N(12)
Deg_To_Rad   4.9(44)
Degree_Sign   A.3.3(22)
DEL   A.3.3(14), J.5(4)
delay_alternative   9.7.1(6)
   used   9.7.1(4), 9.7.2(2), P(1)
delay_relative_statement   9.6(4)
   used   9.6(2), P(1)
delay_statement   9.6(2)
   used   5.1(4), 9.7.1(6), 9.7.4(4), P(1)
delay_until_statement   9.6(3)
   used   9.6(2), P(1)
Delete   A.4.3(29), A.4.3(30), A.4.4(64), A.4.4(65), A.4.5(59), A.4.5(60),
        A.8.1(8), A.8.4(8), A.10.1(11), A.12.1(10)
delimiter   2.2(8)
delivery
   of an interrupt   C.3(2)
delta
   of a fixed point type   3.5.9(1)
Delta attribute   3.5.10(3), K(52)
delta_constraint   J.3(2)
   used   3.2.2(6), P(1)
Denorm attribute   A.5.3(9), K(54)
denormalized number   A.5.3(10)
denote   8.6(16)
   informal definition   3.1(8)
   name used as a pragma argument   8.6(32)
depend on a discriminant
   for a constraint or component_definition   3.7(19)
   for a component   3.7(20)
dependence
   elaboration   10.2(9)
   of a task on a master   9.3(1)
   of a task on another task   9.3(4)
   semantic   10.1.1(26)
depth
   accessibility level   3.10.2(3)
dereference   4.1(8)
Dereference_Error   B.3.1(12)
derivation class
   for a type   3.4.1(2)
derived from
   directly or indirectly   3.4.1(2)
derived type   3.4(1), N(13)
   [partial]   3.4(24)
Derived_From_Formal   12.3(15)
derived_type_definition   3.4(2)
   used   3.2.1(4), P(1)
descendant   10.1.1(11)
   of a type   3.4.1(10)
   relationship with scope   8.2(4)
Descriptor   13.6(5)
designate   3.10(1)
designated profile
   of an access-to-subprogram type   3.10(11)
designated subtype
   of a named access type   3.10(10)
   of an anonymous access type   3.10(12)
designated type
   of a named access type   3.10(10)
   of an anonymous access type   3.10(12)
designator   6.1(5)
   used   6.3(2), P(1)
destructor
   See finalization   7.6(1), 7.6.1(1)
Detach_Handler   C.3.2(9)
determined class for a formal type   12.5(6)
determines
   a type by a subtype_mark   3.2.2(8)
Device   3.8.1(24)
Device_Error   A.8.1(15), A.8.4(18), A.10.1(85), A.12.1(26), A.13(4)
Device_Interface   C.3.2(28)
Device_Priority   C.3.2(28)
Device_Register   13.3(55)
Diaeresis   A.3.3(21)
Dice   A.5.2(56)
Dice_Game   A.5.2(56)
Die   A.5.2(56)
digit   2.1(10)
   used   2.1(3), 2.3(3), 2.4.1(3), 2.4.2(5), P(1)
digits
   of a decimal fixed point subtype   3.5.9(6), 3.5.10(7)
Digits attribute   3.5.8(2), 3.5.10(7), K(56), K(58)
digits_constraint   3.5.9(5)
   used   3.2.2(6), P(1)
dimensionality
   of an array   3.6(12)
direct access   A.8(3)
direct file   A.8(1)
direct_name   4.1(3)
   used   3.8.1(2), 4.1(2), 5.1(8), 9.5.2(3), 13.1(3), J.7(1), P(1)
Direct_IO   J.1(5)
   child of Ada   A.8.4(2), A.9(3)
Direction   A.4.1(6)
directly specified
   of an aspect of representation of an entity   13.1(8)
directly visible   8.3(2), 8.3(21)
   within a pragma in a context_clause   10.1.6(3)
   within a pragma that appears at the place of a compilation unit
        10.1.6(5)
   within a use_clause in a context_clause   10.1.6(3)
   within a with_clause   10.1.6(2)
   within the parent_unit_name of a library unit   10.1.6(2)
   within the parent_unit_name of a subunit   10.1.6(4)
Discard_Names pragma   C.5(3), L(9)
Disconnect   13.13.2(40)
discontiguous representation
   [partial]   13.1(7), 13.5.2(5), 13.7.1(12), 13.9(9), 13.9(17), 13.11(16),
        13.11(17)
discrete array type   4.5.2(1)
Discrete type   3.2(2), 3.2(3), 3.5(1), N(14)
discrete_choice   3.8.1(5)
   used   3.8.1(4), P(1)
discrete_choice_list   3.8.1(4)
   used   3.8.1(3), 4.3.3(5), 5.4(3), P(1)
Discrete_Random
   child of Ada.Numerics   A.5.2(17)
discrete_range   3.6.1(3)
   used   3.6.1(2), 3.8.1(5), 4.1.2(2), P(1)
discrete_subtype_definition   3.6(6)
   used   3.6(5), 5.5(4), 9.5.2(2), 9.5.2(8), P(1)
discriminant   3.2(5), 3.7(1), N(15)
   of a variant_part   3.8.1(6)
discriminant_association   3.7.1(3)
   used   3.7.1(2), P(1)
Discriminant_Check   11.5(12)
   [partial]   4.1.3(15), 4.3(6), 4.3.2(8), 4.6(43), 4.6(45), 4.6(51),
        4.6(52), 4.7(4), 4.8(10)
discriminant_constraint   3.7.1(2)
   used   3.2.2(7), P(1)
discriminant_part   3.7(2)
   used   3.10.1(2), 7.3(2), 7.3(3), 12.5(2), P(1)
discriminant_specification   3.7(5)
   used   3.7(4), P(1)
discriminants
   known   3.7(26)
   unknown   3.7(1), 3.7(26)
discriminated type   3.7(8)
Disk_Unit   3.8.1(27)
dispatching   3.9(3)
dispatching call
   on a dispatching operation   3.9.2(1)
dispatching operation   3.9.2(1), 3.9.2(2)
   [partial]   3.9(1)
dispatching point   D.2.1(4)
   [partial]   D.2.1(8), D.2.2(12)
dispatching policy for tasks   9(10)
   [partial]   D.2.1(5)
dispatching, task   D.2.1(4)
Display_Format   B.4(22)
displayed magnitude (of a decimal value)   F.3.2(14)
disruption of an assignment   9.8(21), 13.9.1(5)
   [partial]   11.6(6)
distinct access paths   6.2(12)
distributed program   E(3)
distributed system   E(2)
distributed systems   C(1)
divide   2.1(15), F.2(6)
divide operator   4.4(1), 4.5.5(1)
Dividend_Type   F.2(6)
Division_Check   11.5(13)
   [partial]   3.5.4(20), 4.5.5(22), A.5.1(28), A.5.3(47), G.1.1(40),
        G.1.2(28), K(202)
Division_Sign   A.3.3(26)
Divisor_Type   F.2(6)
DLE   A.3.3(6), J.5(4)
Do_APC   E.5(10)
Do_RPC   E.5(9)
Do_Something   3.9.3(6)
documentation (required of an implementation)   1.1.3(18), M(1)
documentation requirements   1.1.2(34), 1.1.3(18), 13.11(22), A.5.2(44),
        A.13(15), C.1(6), C.3(12), C.3.2(24), C.4(12), C.7.1(19), C.7.2(18),
        D.2.2(14), D.6(3), D.8(33), D.9(7), D.12(5), E.5(25), H.1(5), H.2(1),
        H.3.2(8), H.4(25), J.7.1(12)
Dollar_Sign   A.3.3(8)
Done   J.7.1(23)
dope   13.5.1(15)
dot   2.1(15)
dot selection
   See selected_component   4.1.3(1)
Dot_Product   6.1(39), 6.3(11)
double   B.3(16)
Double_Precision   B.5(6)
Double_Square   3.7(36)
downward closure   3.10.2(37)
Dozen   4.6(70)
drift rate   D.8(41)
Drum_Ref   3.10(24)
Drum_Unit   3.8.1(27)
Duration   A.1(43)
dynamic binding
   See dispatching operation   3.9(1)
dynamic semantics   1.1.2(30)
Dynamic_Priorities
   child of Ada   D.5(3)
dynamically determined tag   3.9.2(1)
dynamically enclosing
   of one execution by another   11.4(2)
dynamically tagged   3.9.2(5)

E   9.4(20), 9.5.2(13), A.5(3)
edited output   F.3(1)
Editing
   child of Ada.Text_IO   F.3.3(3)
   child of Ada.Wide_Text_IO   F.3.4(1)
Ee   9.4(20)
effect
   external   1.1.3(8)
efficiency   11.5(29), 11.6(1)
elaborable   3.1(11)
Elaborate pragma   10.2.1(20), L(10)
Elaborate_All pragma   10.2.1(21), L(11)
Elaborate_Body pragma   10.2.1(22), L(12)
elaborated   3.11(8)
elaboration   3.1(11), N(19)
   abstract_subprogram_declaration   6.1(31)
   access_definition   3.10(17)
   access_type_definition   3.10(16)
   array_type_definition   3.6(21)
   choice_parameter_specification   11.4(7)
   component_declaration   3.8(17)
   component_definition   3.6(22), 3.8(18)
   component_list   3.8(17)
   declaration named by a pragma Import   B.1(38)
   declarative_part   3.11(7)
   deferred constant declaration   7.4(10)
   delta_constraint   J.3(11)
   derived_type_definition   3.4(26)
   digits_constraint   3.5.9(19)
   discrete_subtype_definition   3.6(22)
   discriminant_constraint   3.7.1(12)
   entry_declaration   9.5.2(22)
   enumeration_type_definition   3.5.1(10)
   exception_declaration   11.1(5)
   fixed_point_definition   3.5.9(17)
   floating_point_definition   3.5.7(13)
   full type definition   3.2.1(11)
   full_type_declaration   3.2.1(11)
   generic body   12.2(2)
   generic_declaration   12.1(10)
   generic_instantiation   12.3(20)
   incomplete_type_declaration   3.10.1(12)
   index_constraint   3.6.1(8)
   integer_type_definition   3.5.4(18)
   loop_parameter_specification   5.5(9)
   non-generic subprogram_body   6.3(6)
   nongeneric package_body   7.2(6)
   number_declaration   3.3.2(7)
   object_declaration   3.3.1(15), 7.6(10)
   package_body of Standard   A.1(50)
   package_declaration   7.1(8)
   partition   E.1(6), E.5(21)
   pragma   2.8(12)
   private_extension_declaration   7.3(17)
   private_type_declaration   7.3(17)
   protected declaration   9.4(12)
   protected_body   9.4(15)
   protected_definition   9.4(13)
   range_constraint   3.5(9)
   real_type_definition   3.5.6(5)
   record_definition   3.8(16)
   record_extension_part   3.9.1(5)
   record_type_definition   3.8(16)
   renaming_declaration   8.5(3)
   representation_clause   13.1(19)
   single_protected_declaration   9.4(12)
   single_task_declaration   9.1(10)
   Storage_Size pragma   13.3(66)
   subprogram_declaration   6.1(31)
   subtype_declaration   3.2.2(9)
   subtype_indication   3.2.2(9)
   task declaration   9.1(10)
   task_body   9.1(13)
   task_definition   9.1(11)
   use_clause   8.4(12)
   variant_part   3.8.1(22)
elaboration control   10.2.1(1)
elaboration dependence
   library_item on another   10.2(9)
Elaboration_Check   11.5(20)
   [partial]   3.11(9)
Elem   12.1(21)
Element   10.1.1(35), A.4.4(26), A.4.5(20), B.3.2(4)
   of a storage pool   13.11(11)
Element_Array   B.3.2(4)
Element_Type   3.9.3(15), A.8.1(2), A.8.4(2), A.9(3)
elementary type   3.2(2), N(16)
Elementary_Functions
   child of Ada.Numerics   A.5.1(9)
eligible
   a type, for a convention   B.1(14)
else part
   of a selective_accept   9.7.1(11)
EM   A.3.3(6)
embedded systems   C(1), D(1)
Empty   3.9.3(15)
encapsulation
   See package   7(1)
enclosing
   immediately   8.1(13)
end of a line   2.2(2)
End_Error   A.8.1(15), A.8.4(18), A.10.1(85), A.12.1(26), A.13(4)
End_Of_File   11.4.2(4), A.8.1(13), A.8.4(16), A.10.1(34), A.12.1(12)
End_Of_Line   A.10.1(30)
End_Of_Page   A.10.1(33)
endian
   big   13.5.3(2)
   little   13.5.3(2)
ENQ   A.3.3(5)
entity   3.1(12)
   [partial]   3.1(1)
entry
   closed   9.5.3(5)
   open   9.5.3(5)
   single   9.5.2(20)
entry call   9.5.3(1)
   simple   9.5.3(1)
entry calling convention   6.3.1(13)
entry family   9.5.2(20)
entry index subtype   3.8(18), 9.5.2(20)
entry queue   9.5.3(12)
entry queuing policy   9.5.3(17)
   default policy   9.5.3(17)
entry_barrier   9.5.2(7)
   used   9.5.2(5), P(1)
entry_body   9.5.2(5)
   used   9.4(8), P(1)
entry_body_formal_part   9.5.2(6)
   used   9.5.2(5), P(1)
entry_call_alternative   9.7.2(3)
   used   9.7.2(2), 9.7.3(2), P(1)
entry_call_statement   9.5.3(2)
   used   5.1(4), 9.7.2(3), 9.7.4(4), P(1)
entry_declaration   9.5.2(2)
   used   9.1(5), 9.4(5), P(1)
entry_index   9.5.2(4)
   used   9.5.2(3), P(1)
entry_index_specification   9.5.2(8)
   used   9.5.2(6), P(1)
Enum   12.5(13), A.10.1(79)
Enum_IO   8.5.5(7)
enumeration literal   3.5.1(6)
Enumeration type   3.2(2), 3.2(3), 3.5.1(1), N(17)
enumeration_aggregate   13.4(3)
   used   13.4(2), P(1)
enumeration_literal_specification   3.5.1(3)
   used   3.5.1(2), P(1)
enumeration_representation_clause   13.4(2)
   used   13.1(2), P(1)
enumeration_type_definition   3.5.1(2)
   used   3.2.1(4), P(1)
Enumeration_IO   A.10.1(79)
environment declarative_part   10.1.4(1)
   for the environment task of a partition   10.2(13)
environment   10.1.4(1)
environment task   10.2(8)
EOF   8.5.2(6)
EOT   A.3.3(5), J.5(4)
EPA   A.3.3(18)
epoch   D.8(19)
equal operator   4.4(1), 4.5.2(1)
equality operator   4.5.2(1)
   special inheritance rule for tagged types   3.4(17), 4.5.2(14)
equals sign   2.1(15)
Equals_Sign   A.3.3(10)
equivalence of use_clauses and selected_components   8.4(1)
erroneous execution   1.1.2(32), 1.1.5(10), 3.7.2(4), 9.8(21), 9.10(11),
        11.5(26), 13.3(13), 13.3(27), 13.9.1(8), 13.9.1(12), 13.11(21),
        13.11.2(16), A.10.3(22), A.13(17), B.3.1(51), B.3.2(35), C.3.1(14),
        C.7.1(18), C.7.2(14), D.5(12), D.11(9), H.4(26)
error   11.1(8)
   compile-time   1.1.2(27), 1.1.5(4)
   link-time   1.1.2(29), 1.1.5(4)
   run-time   1.1.2(30), 1.1.5(6), 11.5(2), 11.6(1)
   See also   bounded error, erroneous execution
ESA   A.3.3(17)
ESC   A.3.3(6)
Establish_RPC_Receiver   E.5(12)
ETB   A.3.3(6)
ETX   A.3.3(5)
evaluable   3.1(11)
evaluation   3.1(11), N(19)
   aggregate   4.3(5)
   allocator   4.8(7)
   array_aggregate   4.3.3(21)
   attribute_reference   4.1.4(11)
   concatenation   4.5.3(5)
   dereference   4.1(13)
   discrete_range   3.6.1(8)
   extension_aggregate   4.3.2(7)
   generic_association   12.3(21)
   generic_association for a formal object of mode in   12.4(11)
   indexed_component   4.1.1(7)
   initialized allocator   4.8(7)
   membership test   4.5.2(27)
   name   4.1(11)
   name that has a prefix   4.1(12)
   null literal   4.2(9)
   numeric literal   4.2(9)
   parameter_association   6.4.1(7)
   prefix   4.1(12)
   primary that is a name   4.4(10)
   qualified_expression   4.7(4)
   range   3.5(9)
   range_attribute_reference   4.1.4(11)
   record_aggregate   4.3.1(18)
   record_component_association_list   4.3.1(19)
   selected_component   4.1.3(14)
   short-circuit control form   4.5.1(7)
   slice   4.1.2(7)
   string_literal   4.2(10)
   uninitialized allocator   4.8(8)
   Val   3.5.5(7), K(261)
   Value   3.5(55)
   value conversion   4.6(28)
   view conversion   4.6(52)
   Wide_Value   3.5(43)
Exception   11(1), 11.1(1), N(18)
exception occurrence   11(1)
exception_choice   11.2(5)
   used   11.2(3), P(1)
exception_declaration   11.1(2)
   used   3.1(3), P(1)
exception_handler   11.2(3)
   used   11.2(2), P(1)
Exception_Identity   11.4.1(5)
Exception_Information   11.4.1(5)
Exception_Message   11.4.1(4)
Exception_Name   11.4.1(2), 11.4.1(5)
Exception_Occurrence   11.4.1(3), 11.4.1(19)
Exception_Occurrence_Access   11.4.1(3)
Exception_Occurrence_Kind   11.4.1(19)
exception_renaming_declaration   8.5.2(2)
   used   8.5(2), P(1)
Exception_Id   11.4.1(2)
Exceptions
   child of Ada   11.4.1(2)
Exchange   12.1(21), 12.2(5)
Exchange_Handler   C.3.2(8)
Exclam   J.5(6)
Exclamation   A.3.3(8)
executable   3.1(11)
execution   3.1(11), N(19)
   abort_statement   9.8(4)
   aborting the execution of a construct   9.8(5)
   accept_statement   9.5.2(24)
   Ada program   9(1)
   assignment_statement   5.2(7), 7.6(17), 7.6.1(12)
   asynchronous_select with a delay_statement trigger   9.7.4(7)
   asynchronous_select with an entry call trigger   9.7.4(6)
   block_statement   5.6(5)
   call on a dispatching operation   3.9.2(14)
   call on an inherited subprogram   3.4(27)
   case_statement   5.4(11)
   conditional_entry_call   9.7.3(3)
   delay_statement   9.6(20)
   dynamically enclosing   11.4(2)
   entry_body   9.5.2(26)
   entry_call_statement   9.5.3(8)
   exit_statement   5.7(5)
   goto_statement   5.8(5)
   handled_sequence_of_statements   11.2(10)
   handler   11.4(7)
   if_statement   5.3(5)
   included by another execution   11.4(2)
   instance of Unchecked_Deallocation   7.6.1(10)
   loop_statement   5.5(7)
   loop_statement with a for iteration_scheme   5.5(9)
   loop_statement with a while iteration_scheme   5.5(8)
   null_statement   5.1(13)
   partition   10.2(25)
   pragma   2.8(12)
   program   10.2(25)
   protected subprogram call   9.5.1(3)
   raise_statement with an exception_name   11.3(4)
   re-raise statement   11.3(4)
   remote subprogram call   E.4(9)
   requeue protected entry   9.5.4(9)
   requeue task entry   9.5.4(8)
   requeue_statement   9.5.4(7)
   return_statement   6.5(6)
   selective_accept   9.7.1(15)
   sequence_of_statements   5.1(15)
   subprogram call   6.4(10)
   subprogram_body   6.3(7)
   task   9.2(1)
   task_body   9.2(1)
   timed_entry_call   9.7.2(4)
execution resource
   associated with a protected object   9.4(18)
   required for a task to run   9(10)
exit_statement   5.7(2)
   used   5.1(4), P(1)
Exp   A.5.1(4), B.1(51), G.1.2(3)
expanded name   4.1.3(4)
Expanded_Name   3.9(7)
expected profile   8.6(26)
   accept_statement entry_direct_name   9.5.2(11)
   Access attribute_reference prefix   3.10.2(2)
   attribute_definition_clause name   13.3(4)
   character_literal   4.2(3)
   formal subprogram actual   12.6(6)
   formal subprogram default_name   12.6(5)
   subprogram_renaming_declaration   8.5.4(3)
expected type   8.6(20)
   abort_statement task_name   9.8(3)
   access attribute_reference   3.10.2(2)
   actual parameter   6.4.1(3)
   aggregate   4.3(3)
   allocator   4.8(3)
   array_aggregate   4.3.3(7)
   array_aggregate component expression   4.3.3(7)
   array_aggregate discrete_choice   4.3.3(8)
   assignment_statement expression   5.2(4)
   assignment_statement variable_name   5.2(4)
   attribute_definition_clause expression or name   13.3(4)
   attribute_designator expression   4.1.4(7)
   case expression   5.4(4)
   case_statement_alternative discrete_choice   5.4(4)
   character_literal   4.2(3)
   code_statement   13.8(4)
   component_clause expressions   13.5.1(7)
   component_declaration default_expression   3.8(7)
   condition   5.3(4)
   decimal fixed point type digits   3.5.9(6)
   delay_relative_statement expression   9.6(5)
   delay_until_statement expression   9.6(5)
   delta_constraint expression   J.3(3)
   dereference name   4.1(8)
   discrete_subtype_definition range   3.6(8)
   discriminant default_expression   3.7(7)
   discriminant_association expression   3.7.1(6)
   entry_index   9.5.2(11)
   enumeration_representation_clause expressions   13.4(4)
   extension_aggregate   4.3.2(4)
   extension_aggregate ancestor expression   4.3.2(4)
   first_bit   13.5.1(7)
   fixed point type delta   3.5.9(6)
   generic formal in object actual   12.4(4)
   generic formal object default_expression   12.4(3)
   index_constraint discrete_range   3.6.1(4)
   indexed_component expression   4.1.1(4)
   Interrupt_Priority pragma argument   D.1(6)
   last_bit   13.5.1(7)
   link name   B.1(10)
   membership test simple_expression   4.5.2(3)
   modular_type_definition expression   3.5.4(5)
   null literal   4.2(2)
   number_declaration expression   3.3.2(3)
   object_declaration initialization expression   3.3.1(4)
   parameter default_expression   6.1(17)
   position   13.5.1(7)
   Priority pragma argument   D.1(6)
   range simple_expressions   3.5(5)
   range_attribute_designator expression   4.1.4(7)
   range_constraint range   3.5(5)
   real_range_specification bounds   3.5.7(5)
   record_aggregate   4.3.1(8)
   record_component_association expression   4.3.1(10)
   requested decimal precision   3.5.7(4)
   restriction parameter expression   13.12(5)
   return expression   6.5(3)
   short-circuit control form relation   4.5.1(1)
   signed_integer_type_definition simple_expression   3.5.4(5)
   slice discrete_range   4.1.2(4)
   Storage_Size pragma argument   13.3(65)
   string_literal   4.2(4)
   type_conversion operand   4.6(6)
   Unchecked_Access attribute   13.10(4)
   variant_part discrete_choice   3.8.1(6)
expiration time
   [partial]   9.6(1)
   for a delay_relative_statement   9.6(20)
   for a delay_until_statement   9.6(20)
explicit declaration   3.1(5), N(11)
explicit initial value   3.3.1(1)
explicit_actual_parameter   6.4(6)
   used   6.4(5), P(1)
explicit_dereference   4.1(5)
   used   4.1(2), P(1)
explicit_generic_actual_parameter   12.3(5)
   used   12.3(4), P(1)
explicitly assign   10.2(2)
exponent   2.4.1(4), 4.5.6(11)
   used   2.4.1(2), 2.4.2(2), P(1)
Exponent attribute   A.5.3(18), K(60)
exponentiation operator   4.4(1), 4.5.6(7)
Export pragma   B.1(6), L(13)
exported
   aspect of representation   B.1(28)
exported entity   B.1(23)
Expr_Ptr   3.9.1(14)
expression   3.9(33), 4.4(1), 4.4(2)
   used   2.8(3), 3.3.1(2), 3.3.2(2), 3.5.4(4), 3.5.7(2), 3.5.9(3), 3.5.9(4),
        3.5.9(5), 3.7(6), 3.7.1(3), 3.8.1(5), 4.1.1(2), 4.1.4(3), 4.1.4(5),
        4.3.1(4), 4.3.2(3), 4.3.3(3), 4.3.3(5), 4.4(7), 4.6(2), 4.7(2),
        5.2(2), 5.3(3), 5.4(2), 6.4(6), 6.5(2), 9.5.2(4), 9.6(3), 9.6(4),
        12.3(5), 13.3(2), 13.3(63), 13.5.1(4), 13.12(4), B.1(5), B.1(6),
        B.1(8), B.1(10), C.3.1(4), D.1(3), D.1(5), J.3(2), J.7(1), J.8(1),
        L(6), L(13), L(14), L(18), L(19), L(27), L(35), P(1)
extended_digit   2.4.2(5)
   used   2.4.2(4), P(1)
extension   12.3(11)
   of a private type   3.9(2), 3.9.1(1)
   of a record type   3.9(2), 3.9.1(1)
   of a type   3.9(2), 3.9.1(1)
extension_aggregate   4.3.2(2)
   used   4.3(2), P(1)
extensions to Ada 83   1.1.2(39), 2.1(18), 2.8(19), 2.8(29), 3.2.3(8),
        3.3(26), 3.3.1(33), 3.3.2(10), 3.4(38), 3.5(63), 3.5.2(9), 3.5.4(36),
        3.5.5(17), 3.5.9(28), 3.6(30), 3.6.1(18), 3.6.3(8), 3.7(37),
        3.7.2(4), 3.8(31), 3.8.1(29), 3.9(33), 3.9.1(17), 3.9.2(24),
        3.10(26), 3.10.1(23), 3.10.2(41), 3.11(14), 4.1(17), 4.1.3(19),
        4.1.4(16), 4.2(14), 4.3(6), 4.3.1(31), 4.3.2(13), 4.3.3(43), 4.4(15),
        4.5.2(39), 4.5.3(14), 4.5.5(35), 4.6(71), 4.8(20), 4.9(44), 5.1(19),
        5.2(28), 5.4(18), 6.1(42), 6.2(13), 6.3(11), 6.3.1(25), 6.3.2(7),
        6.4.1(17), 6.6(9), 7.3(24), 7.4(14), 7.5(23), 7.6(21), 8.2(12),
        8.3(29), 8.4(16), 8.5.5(7), 8.6(34), 9.1(32), 9.4(35), 9.5.2(37),
        9.5.4(20), 9.6(40), 9.7(4), 9.7.4(13), 10.1.1(35), 10.1.2(9),
        10.1.3(24), 10.2(34), 10.2.1(28), 11.2(12), 11.4.1(19), 11.5(31),
        12.1(24), 12.3(29), 12.4(12), 12.5.4(13), 12.7(10), 13.1(24),
        13.3(85), 13.4(14), 13.5.3(8), 13.8(14), 13.9.2(12), 13.11(43),
        13.12(11), 13.13(1), 13.14(19), A.1(56), A.2(4), A.3(1), A.4(1),
        A.5(5), A.5.3(72), A.5.4(4), A.6(1), A.10(11), A.10.1(85), A.11(3),
        A.15(22), B(1), B.1(51), C(1), D(6), D.1(29), E(1), F(7), G(7),
        G.2(3), G.2.1(16), H(6), J.7(2)
external call   9.5(4)
external effect
   of the execution of an Ada program   1.1.3(8)
   volatile/atomic objects   C.6(20)
external file   A.7(1)
external interaction   1.1.3(8)
external name   B.1(34)
external requeue   9.5(7)
External_Tag   3.9(7)
External_Tag attribute   13.3(75), K(64)
External_Tag clause   13.3(7), 13.3(75), K(65)
extra permission to avoid raising exceptions   11.6(5)
extra permission to reorder actions   11.6(6)

F   3.4(38), 3.9.1(4), 3.10.2(22), 5.2(4), 5.4(18), 6.3.1(21), 8.5.4(6),
        8.6(34), 13.14(1), 13.14(13), 13.14(19)
F_View   6.3.1(21)
factor   4.4(6)
   used   4.4(5), P(1)
failure   A.15(8)
   of a language-defined check   11.5(2)
False   3.5.3(1)
family
   entry   9.5.2(20)
Feminine_Ordinal_Indicator   A.3.3(21)
FF   A.3.3(5), J.5(4)
Field   A.10.1(6)
Field_Size   3.9.3(3)
file
   as file object   A.7(2)
file terminator   A.10(7)
File_Access   A.10.1(18)
File_Descriptor   7.5(20)
File_Handle   11.4.2(2)
File_Mode   A.8.1(4), A.8.4(4), A.10.1(4), A.12.1(6)
File_Name   7.3(22), 7.5(18), 7.5(19)
File_Not_Found   11.4.2(3)
File_System   11.4.2(2), 11.4.2(6)
File_Type   A.8.1(3), A.8.4(3), A.10.1(3), A.12.1(5)
Finalization
   child of Ada   7.6(4)
   of a master   7.6.1(4)
   of a protected object   9.4(20), C.3.1(12)
   of a task object   J.7.1(8)
   of an object   7.6.1(5)
Finalize   7.6(2), 7.6(6), 7.6(8), 13.11.3(6), A.5.2(27)
Find   E.4.2(3)
Find_Token   A.4.3(16), A.4.4(51), A.4.5(46)
Fine_Delta   13.7(9)
   named number in package System   13.7(9)
First attribute   3.5(12), 3.6.2(3), K(68), K(70)
first subtype   3.2.1(6), 3.4.1(5)
First(N) attribute   3.6.2(4), K(66)
first_bit   13.5.1(5)
   used   13.5.1(3), P(1)
First_Bit attribute   13.5.2(3), K(72)
Fixed
   child of Ada.Strings   A.4.3(5)
fixed point type   3.5.9(1)
fixed_point_definition   3.5.9(2)
   used   3.5.6(2), P(1)
Fixed_IO   A.10.1(68)
Flip_A_Coin   A.5.2(58)
Float   3.5.7(12), 3.5.7(14), A.1(21)
Float_Random
   child of Ada.Numerics   A.5.2(5)
Float_Text_IO
   child of Ada   A.10.9(32)
Float_Type   A.5.1(3)
Float_Wide_Text_IO
   child of Ada   A.11(3)
Float_IO   A.10.1(63)
Floating   B.4(9)
floating point type   3.5.7(1)
floating_point_definition   3.5.7(2)
   used   3.5.6(2), P(1)
Floor attribute   A.5.3(30), K(74)
Flush   A.10.1(21), A.12.1(25)
Foo   3.9.3(3), 7.3(7), 12.3(15)
Fore attribute   3.5.10(4), K(78)
form   A.8.1(9), A.8.4(9), A.10.1(12), A.12.1(11)
   of an external file   A.7(1)
Formal   12.3(15), 12.3(18)
formal object, generic   12.4(1)
formal package, generic   12.7(1)
formal parameter
   of a subprogram   6.1(17)
formal subprogram, generic   12.6(1)
formal subtype   12.5(5)
formal type   12.5(5)
formal_access_type_definition   12.5.4(2)
   used   12.5(3), P(1)
formal_array_type_definition   12.5.3(2)
   used   12.5(3), P(1)
formal_decimal_fixed_point_definition   12.5.2(7)
   used   12.5(3), P(1)
formal_derived_type_definition   12.5.1(3)
   used   12.5(3), P(1)
formal_discrete_type_definition   12.5.2(2)
   used   12.5(3), P(1)
formal_floating_point_definition   12.5.2(5)
   used   12.5(3), P(1)
formal_modular_type_definition   12.5.2(4)
   used   12.5(3), P(1)
formal_object_declaration   12.4(2)
   used   12.1(6), P(1)
formal_ordinary_fixed_point_definition   12.5.2(6)
   used   12.5(3), P(1)
formal_package_actual_part   12.7(3)
   used   12.7(2), P(1)
formal_package_declaration   12.7(2)
   used   12.1(6), P(1)
formal_part   6.1(14)
   used   6.1(12), 6.1(13), P(1)
formal_private_type_definition   12.5.1(2)
   used   12.5(3), P(1)
formal_signed_integer_type_definition   12.5.2(3)
   used   12.5(3), P(1)
formal_subprogram_declaration   12.6(2)
   used   12.1(6), P(1)
formal_type_declaration   12.5(2)
   used   12.1(6), P(1)
formal_type_definition   12.5(3)
   used   12.5(2), P(1)
format_effector   2.1(13)
   used   2.1(2), P(1)
Fortran
   child of Interfaces   B.5(4)
Fortran interface   B.5(1)
FORTRAN standard   1.2(3)
Fortran_Character   B.5(12)
Fortran_Integer   B.5(5)
Fortran_Library   B.1(51)
Fortran_Matrix   B.5(30)
Fraction   3.5.9(27)
Fraction attribute   A.5.3(21), K(80)
Fraction_One_Half   A.3.3(22)
Fraction_One_Quarter   A.3.3(22)
Fraction_Three_Quarters   A.3.3(22)
Free   13.11.2(5), A.4.5(7), B.3.1(11)
freed
   See nonexistent   13.11.2(10)
freeing storage   13.11.2(1)
freezing
   by a constituent of a construct   13.14(4)
   by an expression   13.14(8)
   class-wide type caused by the freezing of the specific type   13.14(15)
   constituents of a full type definition   13.14(15)
   designated subtype caused by an allocator   13.14(13)
   entity   13.14(2)
   entity caused by a body   13.14(3)
   entity caused by a construct   13.14(4)
   entity caused by a name   13.14(11)
   entity caused by the end of an enclosing construct   13.14(3)
   first subtype caused by the freezing of the type   13.14(15)
   function call   13.14(14)
   generic_instantiation   13.14(5)
   nominal subtype caused by a name   13.14(11)
   object_declaration   13.14(6)
   specific type caused by the freezing of the class-wide type   13.14(15)
   subtype caused by a record extension   13.14(7)
   subtypes of the profile of a callable entity   13.14(14)
   type caused by a range   13.14(12)
   type caused by an expression   13.14(10)
   type caused by the freezing of a subtype   13.14(15)
freezing points
   entity   13.14(2)
FS   A.3.3(6), J.5(4)
full conformance
   for discrete_subtype_definitions   6.3.1(24)
   for known_discriminant_parts   6.3.1(23)
   for expressions   6.3.1(19)
   for profiles   6.3.1(18)
   required   3.10.1(4), 6.3(4), 7.3(9), 8.5.4(5), 9.5.2(14), 9.5.2(16),
        9.5.2(17), 10.1.3(11), 10.1.3(12)
full constant declaration   3.3.1(6)
full declaration   7.4(2)
full stop   2.1(15)
full type   3.2.1(8)
full type definition   3.2.1(8)
full view
   of a type   7.3(4)
Full_Stop   A.3.3(8)
full_type_declaration   3.2.1(3)
   used   3.2.1(2), P(1)
function   6(1)
function instance   12.3(13)
function_call   6.4(3)
   used   4.1(2), P(1)

G   3.10.2(22), 4.9(26), 12.3(15), 12.3(18), 12.3(22), 13.14(1)
G1   12.3(11)
G2   12.3(11)
gaps   13.1(7), 13.3(52)
garbage collection   13.11.3(6)
Gender   3.5.1(14)
general access type   3.10(7), 3.10(8)
general_access_modifier   3.10(4)
   used   3.10(3), P(1)
generation
   of an interrupt   C.3(2)
Generator   A.5.2(7), A.5.2(19), A.5.2(27)
generic actual   12.3(7)
generic actual parameter   12.3(7)
generic actual subtype   12.5(4)
generic actual type   12.5(4)
generic body   12.2(1)
generic contract issue   10.2.1(10), 12.3(11)
   [partial]   3.9.1(3), 3.10.2(28), 3.10.2(32), 4.6(17), 4.6(20), 6.3.1(17),
        6.5(20), 8.3(26), 10.2.1(11)
generic contract model   12.3(1)
generic contract/private type contract analogy   7.3(19)
generic formal   12.1(9)
generic formal object   12.4(1)
generic formal package   12.7(1)
generic formal subprogram   12.6(1)
generic formal subtype   12.5(5)
generic formal type   12.5(5)
generic function   12.1(8)
generic package   12.1(8)
generic procedure   12.1(8)
generic subprogram   12.1(8)
generic unit   12(1), N(20)
   See also dispatching operation   3.9(1)
generic_actual_part   12.3(3)
   used   12.3(2), 12.7(3), P(1)
generic_association   12.3(4)
   used   12.3(3), P(1)
Generic_Bags   10.1.1(35)
Generic_Bags.Generic_Iterators   10.1.1(35)
Generic_Bounded_Length   A.4.4(4)
Generic_Complex_Elementary_Functions
   child of Ada.Numerics   G.1.2(2)
Generic_Complex_Types
   child of Ada.Numerics   G.1.1(2)
generic_declaration   12.1(2)
   used   3.1(3), 10.1.1(5), P(1)
Generic_Elementary_Functions
   child of Ada.Numerics   A.5.1(3)
generic_formal_parameter_declaration   12.1(6)
   used   12.1(5), P(1)
generic_formal_part   12.1(5)
   used   12.1(3), 12.1(4), P(1)
generic_instantiation   12.3(2)
   used   3.1(3), 10.1.1(5), P(1)
generic_package_declaration   12.1(4)
   used   12.1(2), P(1)
generic_renaming_declaration   8.5.5(2)
   used   8.5(2), 10.1.1(6), P(1)
generic_subprogram_declaration   12.1(3)
   used   12.1(2), P(1)
Get   10.1.1(30), A.10.1(41), A.10.1(47), A.10.1(54), A.10.1(55), A.10.1(59),
        A.10.1(60), A.10.1(65), A.10.1(67), A.10.1(70), A.10.1(72),
        A.10.1(75), A.10.1(77), A.10.1(81), A.10.1(83), G.1.3(6), G.1.3(8)
Get_Immediate   A.10.1(44), A.10.1(45)
Get_Key   7.3.1(15), 7.3.1(16)
Get_Line   A.10.1(49)
Get_Next   3.6(11)
Get_Priority   D.5(5)
Global   9.3(20)
global to   8.1(15)
Glossary   N(1)
Good_1   12.3(11)
Good_2   12.3(11)
goto_statement   5.8(2)
   used   5.1(4), P(1)
govern a variant_part   3.8.1(20)
govern a variant   3.8.1(20)
Gp   3.9.1(4)
grammar
   ambiguous   1.1.4(14)
   complete listing   P(1)
   cross reference   P(1)
   notation   1.1.4(3)
   resolution of ambiguity   1.1.4(14), 8.6(3)
   under Syntax heading   1.1.2(25)
graphic character
   a category of Character   A.3.2(23)
graphic_character   2.1(3)
   used   2.1(2), 2.5(2), 2.6(3), P(1)
Graphic_Set   A.4.6(4)
greater than operator   4.4(1), 4.5.2(1)
greater than or equal operator   4.4(1), 4.5.2(1)
greater-than sign   2.1(15)
Greater_Than_Sign   A.3.3(10)
GS   A.3.3(6)
guard   9.7.1(3)
   used   9.7.1(2), P(1)

Half_Pi   4.9(44)
handle
   an exception   11(1), N(18)
   an exception occurrence   11(1), 11.4(1), 11.4(7)
handled_sequence_of_statements   11.2(2)
   used   5.6(2), 6.3(2), 7.2(2), 9.1(6), 9.5.2(3), 9.5.2(5), P(1)
handler   11.2(5), C.3.2(28)
Handling
   child of Ada.Characters   A.3.2(2)
Hash_Index   3.5.4(36)
head (of a queue)   D.2.1(5)
Head   A.4.3(35), A.4.3(36), A.4.4(70), A.4.4(71), A.4.5(65), A.4.5(66)
heap management
   See also alligator   4.8(1)
   user-defined   13.11(1)
held priority   D.11(4)
Hello   3.3.1(31)
heterogeneous input-output   A.12.1(1)
Hexa   3.5.1(15)
hexadecimal
   literal   2.4.2(1)
hexadecimal digit
   a category of Character   A.3.2(30)
hexadecimal literal   2.4.2(1)
Hexadecimal_Digit_Set   A.4.6(4)
hidden from all visibility   8.3(5), 8.3(14)
   by lack of a with_clause   8.3(20)
   for a declaration completed by a subsequent declaration   8.3(19)
   for overridden declaration   8.3(15)
   within the declaration itself   8.3(16)
hidden from direct visibility   8.3(5), 8.3(21)
   by an inner homograph   8.3(22)
   where hidden from all visibility   8.3(23)
hiding   8.3(5)
High_Order_First   13.5.3(2), B.4(25)
highest precedence operator   4.5.6(1)
highest_precedence_operator   4.5(7)
Hold   D.11(3)
homograph   8.3(8)
HT   A.3.3(5)
HTJ   A.3.3(17)
HTS   A.3.3(17)
Hyphen   A.3.3(8)
hyphen-minus   2.1(15)

I   3.9.1(4), 4.9(26), 12.3(22), G.1.1(5), G.1.1(23)
identifier   2.3(2)
   used   2.8(2), 2.8(3), 2.8(21), 2.8(23), 3.1(4), 4.1(3), 4.1.3(3),
        4.1.4(3), 5.5(2), 5.6(2), 6.1(5), 7.1(3), 7.2(2), 9.1(4), 9.1(6),
        9.4(4), 9.4(7), 9.5.2(3), 9.5.2(5), 11.5(4), 13.12(4), B.1(5),
        B.1(6), B.1(7), D.2.2(2), D.2.2(3), D.3(3), D.3(4), D.4(3), D.4(4),
        L(8), L(13), L(14), L(20), L(21), L(23), L(29), L(36), L(37), M(95),
        M(98), P(1)
identifier specific to a pragma   2.8(10)
identifier_letter   2.1(7)
   used   2.1(3), 2.3(2), 2.3(3), P(1)
Identity   A.4.2(22), A.4.7(22)
Identity attribute   11.4.1(9), C.7.1(12), K(84), K(86)
idle task   D.11(4)
IEC 559:1989   G.2.2(11)
IEEE floating point arithmetic   B.2(10), G.2.2(11)
if_statement   5.3(2)
   used   5.1(5), P(1)
illegal
   construct   1.1.2(27)
   partition   1.1.2(29)
Im   10.1.1(35), G.1.1(6)
image   10.1.1(35), A.5.2(14), A.5.2(26), C.7.1(3), F.3.3(13)
   of a value   3.5(30), K(273)
Image attribute   3.5(35), K(88)
Imaginary   B.5(10), G.1.1(4), G.1.1(23)
immediate scope
   of (a view of) an entity   8.2(11)
   of a declaration   8.2(2)
immediately enclosing   8.1(13)
immediately visible   8.3(4), 8.3(21)
immediately within   8.1(13)
implementation   1.1.3(1)
implementation advice   1.1.2(37)
implementation defined   1.1.3(18)
   summary of characteristics   M(1)
implementation permissions   1.1.2(36)
implementation requirements   1.1.2(33)
implementation-dependent
   See unspecified   1.1.3(18)
implicit declaration   3.1(5), N(11)
implicit initial values
   for a subtype   3.3.1(10)
implicit subtype conversion   4.6(59), 4.6(60)
   Access attribute   3.10.2(30)
   access discriminant   3.7(27)
   array bounds   4.6(38)
   array index   4.1.1(7)
   assignment to view conversion   4.6(55)
   assignment_statement   5.2(11)
   bounds of a decimal fixed point type   3.5.9(16)
   bounds of a fixed point type   3.5.9(14)
   bounds of a floating point type   3.5.7(11)
   bounds of a range   3.5(9), 3.6(18)
   bounds of signed integer type   3.5.4(9)
   choices of aggregate   4.3.3(22)
   component defaults   3.3.1(13)
   delay expression   9.6(20)
   derived type discriminants   3.4(21)
   discriminant values   3.7.1(12)
   entry index   9.5.2(24)
   expressions in aggregate   4.3.1(19)
   expressions of aggregate   4.3.3(23)
   function return   6.5(6)
   generic formal object of mode in   12.4(11)
   inherited enumeration literal   3.4(29)
   initialization expression   3.3.1(17)
   initialization expression of allocator   4.8(7)
   named number value   3.3.2(6)
   operand of concatenation   4.5.3(9)
   parameter passing   6.4.1(10), 6.4.1(11), 6.4.1(17)
   pragma Interrupt_Priority   D.1(17), D.3(9)
   pragma Priority   D.1(17), D.3(9)
   qualified_expression   4.7(4)
   reading a view conversion   4.6(56)
   result of inherited function   3.4(27)
implicit_dereference   4.1(6)
   used   4.1(4), P(1)
Import pragma   B.1(5), L(14)
imported
   aspect of representation   B.1(28)
imported entity   B.1(23)
in (membership test)   4.4(1), 4.5.2(2)
inaccessible partition   E.1(7)
inactive
   a task state   9(10)
included
   one execution by another   11.4(2)
   one range in another   3.5(4)
incompatibilities with Ada 83   1.1.2(39), 2.8(19), 2.9(3), 3.2.2(15),
        3.2.3(8), 3.4(38), 3.5(63), 3.5.2(9), 3.6.3(8), 4.2(14), 4.6(71),
        4.8(20), 4.9(44), 6.5(24), 7.1(17), 8.6(34), 12.3(29), 12.5.1(28),
        12.5.3(16), 12.5.4(13), 13.1(24), 13.14(19), A.5.3(72), A.5.4(4),
        A.8.1(16), A.10.1(85), C.6(22)
incomplete type   3.10.1(11)
incomplete_type_declaration   3.10.1(2)
   used   3.2.1(2), P(1)
inconsistencies with Ada 83   1.1.2(39), 3.4(38), 3.5.2(9), 3.5.7(22),
        3.5.9(28), 3.6.3(8), 3.7.1(15), 4.5.3(14), 9.6(40), 11.1(8),
        12.3(29), A.6(1), G.2.1(16), G.2.3(27)
Increment   6.1(37), B.3.2(11)
indefinite subtype   3.3(23), 3.7(26)
independent subprogram   11.6(6)
independently addressable   9.10(1)
index   12.1(19), 12.5.3(11), A.4.3(9), A.4.3(10), A.4.3(11), A.4.4(44),
        A.4.4(45), A.4.4(46), A.4.5(39), A.4.5(40), A.4.5(41), A.8.4(15),
        A.12.1(23), B.3.2(4)
   of an array   3.6(9)
   of an element of an open direct file   A.8(3)
index range   3.6(13)
index subtype   3.6(9)
index type   3.6(9)
Index_Check   11.5(14)
   [partial]   4.1.1(7), 4.1.2(7), 4.3.3(29), 4.3.3(30), 4.5.3(8), 4.6(51),
        4.7(4), 4.8(10)
index_constraint   3.6.1(2)
   used   3.2.2(7), P(1)
Index_Non_Blank   A.4.3(12), A.4.4(47), A.4.5(42)
index_subtype_definition   3.6(4)
   used   3.6(3), P(1)
indexed_component   4.1.1(2)
   used   4.1(2), P(1)
indivisible   C.6(10)
information hiding
   See package   7(1)
   See private types and private extensions   7.3(1)
information systems   C(1), F(1)
informative   1.1.2(18)
inheritance
   See also tagged types and type extension   3.9(1)
   See derived types and classes   3.4(1)
inherited
   from an ancestor type   3.4.1(11)
inherited component   3.4(11), 3.4(12)
inherited discriminant   3.4(11)
inherited entry   3.4(12)
inherited protected subprogram   3.4(12)
inherited subprogram   3.4(17)
initialization
   of a protected object   9.4(14), C.3.1(10), C.3.1(11)
   of a task object   9.1(12), J.7.1(7)
   of an object   3.3.1(19)
initialization expression   3.3.1(1), 3.3.1(4)
Initialize   7.6(2), 7.6(6), 7.6(8)
Initialize_Generator   A.5.2(60)
initialized allocator   4.8(4)
Inline pragma   6.3.2(3), L(15)
Inner   9.5.2(13), 10.1.3(20), 10.1.3(21), 10.1.3(23), 10.1.3(24), 13.14(19)
innermost dynamically enclosing   11.4(2)
input   A.6(1)
Input attribute   13.13.2(22), 13.13.2(32), K(92), K(96)
Input clause   13.3(7), 13.13.2(36)
input-output
   unspecified for access types   A.7(6)
Insert   A.4.3(25), A.4.3(26), A.4.4(60), A.4.4(61), A.4.5(55), A.4.5(56)
inspectable object   H.3.2(5)
inspection point   H.3.2(5)
Inspection_Point pragma   H.3.2(3), L(16)
Inst   12.3(15)
instance   12.3(18)
   of a generic function   12.3(13)
   of a generic package   12.3(13)
   of a generic procedure   12.3(13)
   of a generic subprogram   12.3(13)
   of a generic unit   12.3(1)
instructions for comment submission   (59)
Int   3.2.2(15), 9.5.2(13), 12.5(13), B.3(7)
Int_Plus   8.5.4(15)
Int_Ptr   3.10.2(22)
Int_Vectors   12.3(25)
Int_IO   A.10.8(26)
Int_Op   7.3.1(7)
Int10   4.9(26)
Integer   3.5.4(11), 3.5.4(21), A.1(12)
integer literal   2.4(1)
integer literals   3.5.4(14), 3.5.4(30)
Integer type   3.2(2), 3.5.4(1), N(21)
Integer_Address   13.7.1(10)
Integer_Text_IO
   child of Ada   A.10.8(20)
integer_type_definition   3.5.4(2)
   used   3.2.1(4), P(1)
Integer_Wide_Text_IO
   child of Ada   A.11(3)
Integer_IO   A.10.1(52)
interaction
   between tasks   9(1)
interface to assembly language   C.1(4)
interface to C   B.3(1)
interface to COBOL   B.4(1)
interface to Fortran   B.5(1)
interface to other languages   B(1)
Interfaces   B.2(3)
Interfaces.COBOL   B.4(7)
Interfaces.Fortran   B.2(13), B.5(4)
Interfaces.C   B.3(4)
Interfaces.C.Pointers   B.3.2(4)
Interfaces.C.Strings   B.3.1(3)
interfacing pragma   B.1(4)
   Convention   B.1(4)
   Export   B.1(4)
   Import   B.1(4)
internal call   9.5(3)
internal code   13.4(7)
internal requeue   9.5(7)
Internal_Tag   3.9(7)
interpretation
   of a complete context   8.6(10)
   of a constituent of a complete context   8.6(15)
   overload resolution   8.6(14)
interrupt   C.3(2)
   example using asynchronous_select   9.7.4(10), 9.7.4(12)
interrupt entry   J.7.1(5)
interrupt handler   C.3(2)
Interrupt_Handler   J.7.1(23)
Interrupt_Handler pragma   C.3.1(2), L(17)
Interrupt_Priority   13.7(16), D.1(10)
Interrupt_Priority pragma   D.1(5), L(18)
Interrupt_ID   C.3.2(2)
Interrupts
   child of Ada   C.3.2(2)
Intersection   3.9.3(15)
intertask communication   9.5(1)
   See also task   9(1)
Intrinsic calling convention   6.3.1(4)
invalid representation   13.9.1(9)
Invert   B.5(30)
Inverted_Exclamation   A.3.3(21)
Inverted_Question   A.3.3(22)
IO   6.3.2(5)
IO_Exceptions   J.1(7)
   child of Ada   A.13(3)
IO_Package   7.5(18), 7.5(20)
Is_Alphanumeric   A.3.2(4)
Is_Attached   C.3.2(5)
Is_Basic   A.3.2(4)
Is_Callable   C.7.1(4)
Is_Character   A.3.2(14)
Is_Control   A.3.2(4)
Is_Decimal_Digit   A.3.2(4)
Is_Digit   A.3.2(4)
Is_Graphic   A.3.2(4)
Is_Held   D.11(3)
Is_Hexadecimal_Digit   A.3.2(4)
Is_ISO_646   A.3.2(10)
Is_Letter   A.3.2(4)
Is_Lower   A.3.2(4)
Is_Open   A.8.1(10), A.8.4(10), A.10.1(13), A.12.1(12)
Is_Reserved   C.3.2(4)
Is_Special   A.3.2(4)
Is_String   A.3.2(14)
Is_Subset   A.4.2(14), A.4.7(14)
Is_Terminated   C.7.1(4)
Is_Upper   A.3.2(4)
Is_In   A.4.2(13), A.4.7(13)
ISO 10646   3.5.2(2), 3.5.2(3)
ISO 1989:1985   1.2(4)
ISO/IEC 10646-1:1993   1.2(8)
ISO/IEC 1539:1991   1.2(3)
ISO/IEC 6429:1992   1.2(5)
ISO/IEC 646:1991   1.2(2)
ISO/IEC 8859-1:1987   1.2(6)
ISO/IEC 9899:1990   1.2(7)
ISO_646   A.3.2(9)
ISO_646_Set   A.4.6(4)
issue
   an entry call   9.5.3(8)
italics
   formal parameters of attribute functions   3.5(18)
   implementation-defined   1.1.3(5)
   nongraphic characters   3.5.2(2)
   pseudo-names of anonymous types   3.2.1(7), A.1(2)
   syntax rules   1.1.4(14)
   terms introduced or defined   1.3(1)
italics, like this   1(2)
Item   3.7(37), 12.1(19), 12.1(22), 12.1(24), 12.5(12), 12.5.3(11), 12.8(3),
        12.8(14)
Iterate   10.1.1(35), 12.6(20)
iteration_scheme   5.5(3)
   used   5.5(2), P(1)
Iterators_Of_Bags_Of_My_Type   10.1.1(35)
Iters   10.1.1(35)

j   G.1.1(5), G.1.1(23)

Key   7.3(22), 7.3.1(15)
Key_Manager   7.3.1(15), 7.3.1(16)
Keyboard   9.1(32)
Keyboard_Driver   9.1(24)
Kilo   4.9(43)
known discriminants   3.7(26)
known_discriminant_part   3.7(4)
   used   3.2.1(3), 3.7(2), 9.1(2), 9.4(2), P(1)

L_Brace   J.5(6)
L_Bracket   J.5(6)
label   5.1(7)
   used   5.1(3), P(1)
language
   interface to assembly   C.1(4)
   interface to non-Ada   B(1)
language-defined check   11.5(2), 11.6(1)
language-defined class
   [partial]   3.2(10)
   of types   3.2(2)
Language-Defined Library Units   A(1)
   Ada   A.2(2)
   Ada.Asynchronous_Task_Control   D.11(3)
   Ada.Calendar   9.6(10)
   Ada.Characters   A.3.1(2)
   Ada.Characters.Handling   A.3.2(2)
   Ada.Characters.Latin_1   A.3.3(3)
   Ada.Command_Line   A.15(3)
   Ada.Decimal   F.2(2)
   Ada.Direct_IO   A.8.4(2), A.9(3)
   Ada.Dynamic_Priorities   D.5(3)
   Ada.Exceptions   11.4.1(2)
   Ada.Finalization   7.6(4)
   Ada.Float_Text_IO   A.10.9(32)
   Ada.Float_Wide_Text_IO   A.11(3)
   Ada.Integer_Text_IO   A.10.8(20)
   Ada.Integer_Wide_Text_IO   A.11(3)
   Ada.Interrupts   C.3.2(2)
   Ada.Interrupts.Names   C.3.2(12)
   Ada.IO_Exceptions   A.13(3)
   Ada.Numerics   A.5(3)
   Ada.Numerics.Complex_Elementary_Functions   G.1.2(9)
   Ada.Numerics.Complex_Types   G.1.1(25)
   Ada.Numerics.Discrete_Random   A.5.2(17)
   Ada.Numerics.Elementary_Functions   A.5.1(9)
   Ada.Numerics.Float_Random   A.5.2(5)
   Ada.Numerics.Generic_Complex_Elementary_Functions   G.1.2(2)
   Ada.Numerics.Generic_Complex_Types   G.1.1(2)
   Ada.Numerics.Generic_Elementary_Functions   A.5.1(3)
   Ada.Real_Time   D.8(3)
   Ada.Sequential_IO   A.8.1(2)
   Ada.Storage_IO   A.9(3)
   Ada.Streams   13.13.1(2)
   Ada.Streams.Stream_IO   A.12.1(3)
   Ada.Strings   A.4.1(3)
   Ada.Strings.Bounded   A.4.4(3)
   Ada.Strings.Fixed   A.4.3(5)
   Ada.Strings.Maps   A.4.2(3)
   Ada.Strings.Maps.Constants   A.4.6(3)
   Ada.Strings.Unbounded   A.4.5(3)
   Ada.Strings.Wide_Bounded   A.4.7(1)
   Ada.Strings.Wide_Fixed   A.4.7(1)
   Ada.Strings.Wide_Maps   A.4.7(3)
   Ada.Strings.Wide_Maps.Wide_Constants   A.4.7(1)
   Ada.Strings.Wide_Unbounded   A.4.7(1)
   Ada.Synchronous_Task_Control   D.10(3)
   Ada.Tags   3.9(6)
   Ada.Task_Attributes   C.7.2(2)
   Ada.Task_Identification   C.7.1(2)
   Ada.Text_IO   A.10.1(2)
   Ada.Text_IO.Complex_IO   G.1.3(3)
   Ada.Text_IO.Editing   F.3.3(3)
   Ada.Text_IO.Text_Streams   A.12.2(3)
   Ada.Unchecked_Conversion   13.9(3)
   Ada.Unchecked_Deallocation   13.11.2(3)
   Ada.Wide_Text_IO   A.11(2)
   Ada.Wide_Text_IO.Complex_IO   G.1.4(1)
   Ada.Wide_Text_IO.Editing   F.3.4(1)
   Ada.Wide_Text_IO.Text_Streams   A.12.3(3)
   Interfaces   B.2(3)
   Interfaces.C   B.3(4)
   Interfaces.C.Pointers   B.3.2(4)
   Interfaces.C.Strings   B.3.1(3)
   Interfaces.COBOL   B.4(7)
   Interfaces.Fortran   B.5(4)
   Standard   A.1(4)
   System   13.7(3)
   System.Address_To_Access_Conversions   13.7.2(2)
   System.Machine_Code   13.8(7)
   System.RPC   E.5(3)
   System.Storage_Elements   13.7.1(2)
   System.Storage_Pools   13.11(5)
Language-Defined Types
   Address, in System   13.7(12)
   Alignment, in Ada.Strings   A.4.1(6)
   Alphanumeric, in Interfaces.COBOL   B.4(16)
   Attribute_Handle, in Ada.Task_Attributes   C.7.2(3)
   Binary, in Interfaces.COBOL   B.4(10)
   Binary_Format, in Interfaces.COBOL   B.4(24)
   Bit_Order, in System   13.7(15)
   Boolean, in Standard   A.1(5)
   Bounded_String, in Ada.Strings.Bounded.Generic_Bounded_Length   A.4.4(6)
   Byte, in Interfaces.COBOL   B.4(29)
   Byte_Array, in Interfaces.COBOL   B.4(29)
   C_float, in Interfaces.C   B.3(15)
   char, in Interfaces.C   B.3(19)
   char_array, in Interfaces.C   B.3(23)
   char_array_access, in Interfaces.C   B.3.1(4)
   Character, in Standard   A.1(35)
   Character_Set, in Ada.Strings.Maps   A.4.2(4)
   chars_ptr, in Interfaces.C   B.3.1(5)
   chars_ptr_array, in Interfaces.C   B.3.1(6)
   COBOL_Character, in Interfaces.COBOL   B.4(13)
   Complex, in Ada.Numerics.Generic_Complex_Types   G.1.1(3)
   Controlled, in Ada.Finalization   7.6(5)
   Count, in Ada.Direct_IO   A.8.4(4)
   Count, in Ada.Text_IO   A.10.1(5)
   Decimal_Element, in Interfaces.COBOL   B.4(12)
   Direction, in Ada.Strings   A.4.1(6)
   Display_Format, in Interfaces.COBOL   B.4(22)
   double, in Interfaces.C   B.3(16)
   Duration, in Standard   A.1(43)
   Exception_Occurrence, in Ada.Exceptions   11.4.1(3)
   Exception_Occurrence_Access, in Ada.Exceptions   11.4.1(3)
   Exception_Id, in Ada.Exceptions   11.4.1(2)
   File_Mode, in Ada.Direct_IO   A.8.4(4)
   File_Mode, in Ada.Sequential_IO   A.8.1(4)
   File_Mode, in Ada.Text_IO   A.10.1(4)
   File_Type, in Ada.Direct_IO   A.8.4(3)
   File_Type, in Ada.Sequential_IO   A.8.1(3)
   File_Type, in Ada.Text_IO   A.10.1(3)
   Float, in Standard   A.1(21)
   Floating, in Interfaces.COBOL   B.4(9)
   Generator, in Ada.Numerics.Discrete_Random   A.5.2(19)
   Generator, in Ada.Numerics.Float_Random   A.5.2(7)
   Imaginary, in Ada.Numerics.Generic_Complex_Types   G.1.1(4)
   int, in Interfaces.C   B.3(7)
   Integer, in Standard   A.1(12)
   Integer_Address, in System.Storage_Elements   13.7.1(10)
   Interrupt_ID, in Ada.Interrupts   C.3.2(2)
   Limited_Controlled, in Ada.Finalization   7.6(7)
   long, in Interfaces.C   B.3(7)
   Long_Binary, in Interfaces.COBOL   B.4(10)
   long_double, in Interfaces.C   B.3(17)
   Long_Floating, in Interfaces.COBOL   B.4(9)
   Membership, in Ada.Strings   A.4.1(6)
   Name, in System   13.7(4)
   Numeric, in Interfaces.COBOL   B.4(20)
   Packed_Decimal, in Interfaces.COBOL   B.4(12)
   Packed_Format, in Interfaces.COBOL   B.4(26)
   Parameterless_Handler, in Ada.Interrupts   C.3.2(2)
   Partition_ID, in System.RPC   E.5(4)
   Picture, in Ada.Text_IO.Editing   F.3.3(4)
   Picture, in Ada.Wide_Text_IO.Editing   F.3.4(1)
   plain_char, in Interfaces.C   B.3(11)
   Pointer, in Interfaces.C.Pointers   B.3.2(5)
   ptrdiff_t, in Interfaces.C   B.3(12)
   Root_Storage_Pool, in System.Storage_Pools   13.11(6)
   Root_Stream_Type, in Ada.Streams   13.13.1(3)
   Seconds_Count, in Ada.Real_Time   D.8(15)
   short, in Interfaces.C   B.3(7)
   signed_char, in Interfaces.C   B.3(8)
   size_t, in Interfaces.C   B.3(13)
   State, in Ada.Numerics.Discrete_Random   A.5.2(23)
   State, in Ada.Numerics.Float_Random   A.5.2(11)
   Storage_Array, in System.Storage_Elements   13.7.1(5)
   Storage_Element, in System.Storage_Elements   13.7.1(5)
   Storage_Offset, in System.Storage_Elements   13.7.1(3)
   Stream_Access, in Ada.Streams.Stream_IO   A.12.1(4)
   String, in Standard   A.1(37)
   Suspension_Object, in Ada.Synchronous_Task_Control   D.10(4)
   Tag, in Tags   3.9(6)
   Task_ID, in Ada.Task_Identification   C.7.1(2)
   Time, in Ada.Calendar   9.6(10)
   Time, in Ada.Real_Time   D.8(4)
   Time_Span, in Ada.Real_Time   D.8(6)
   Trim_End, in Ada.Strings   A.4.1(6)
   Truncation, in Ada.Strings   A.4.1(6)
   Type_Set, in Ada.Text_IO   A.10.1(7)
   Unbounded_String, in Ada.Strings.Unbounded   A.4.5(4)
   unsigned, in Interfaces.C   B.3(9)
   unsigned_char, in Interfaces.C   B.3(10)
   unsigned_long, in Interfaces.C   B.3(9)
   unsigned_short, in Interfaces.C   B.3(9)
   wchar_array, in Interfaces.C   B.3(33)
   wchar_t, in Interfaces.C   B.3(30)
   Wide_Character, in Standard   A.1(36)
   Wide_Character_Set, in Ada.Strings.Wide_Maps   A.4.7(4)
   Wide_String, in Standard   A.1(41)
Last attribute   3.5(13), 3.6.2(5), K(102), K(104)
Last(N) attribute   3.6.2(6), K(100)
last_bit   13.5.1(6)
   used   13.5.1(3), P(1)
Last_Bit attribute   13.5.2(4), K(106)
lateness   D.9(12)
Latin-1   3.5.2(2)
Latin_1
   child of Ada.Characters   A.3.3(3)
layout
   aspect of representation   13.5(1)
Layout_Error   A.10.1(85), A.13(4)
LC_German_Sharp_S   A.3.3(24)
LC_Icelandic_Eth   A.3.3(26)
LC_Icelandic_Thorn   A.3.3(26)
LC_A   A.3.3(13), J.5(8)
LC_A_Acute   A.3.3(25)
LC_A_Circumflex   A.3.3(25)
LC_A_Diaeresis   A.3.3(25)
LC_A_Grave   A.3.3(25)
LC_A_Ring   A.3.3(25)
LC_A_Tilde   A.3.3(25)
LC_AE_Diphthong   A.3.3(25)
LC_B   A.3.3(13)
LC_C   A.3.3(13)
LC_C_Cedilla   A.3.3(25)
LC_D   A.3.3(13)
LC_E   A.3.3(13)
LC_E_Acute   A.3.3(25)
LC_E_Circumflex   A.3.3(25)
LC_E_Diaeresis   A.3.3(25)
LC_E_Grave   A.3.3(25)
LC_F   A.3.3(13)
LC_G   A.3.3(13)
LC_H   A.3.3(13)
LC_I   A.3.3(13)
LC_I_Acute   A.3.3(25)
LC_I_Circumflex   A.3.3(25)
LC_I_Diaeresis   A.3.3(25)
LC_I_Grave   A.3.3(25)
LC_J   A.3.3(13)
LC_K   A.3.3(13)
LC_L   A.3.3(13)
LC_M   A.3.3(13)
LC_N   A.3.3(13)
LC_N_Tilde   A.3.3(26)
LC_O   A.3.3(13)
LC_O_Acute   A.3.3(26)
LC_O_Circumflex   A.3.3(26)
LC_O_Diaeresis   A.3.3(26)
LC_O_Grave   A.3.3(26)
LC_O_Oblique_Stroke   A.3.3(26)
LC_O_Tilde   A.3.3(26)
LC_P   A.3.3(14)
LC_Q   A.3.3(14)
LC_R   A.3.3(14)
LC_S   A.3.3(14)
LC_T   A.3.3(14)
LC_U   A.3.3(14)
LC_U_Acute   A.3.3(26)
LC_U_Circumflex   A.3.3(26)
LC_U_Diaeresis   A.3.3(26)
LC_U_Grave   A.3.3(26)
LC_V   A.3.3(14)
LC_W   A.3.3(14)
LC_X   A.3.3(14)
LC_Y   A.3.3(14)
LC_Y_Acute   A.3.3(26)
LC_Y_Diaeresis   A.3.3(26)
LC_Z   A.3.3(14), J.5(8)
Leading_Nonseparate   B.4(23)
Leading_Part attribute   A.5.3(54), K(108)
Leading_Separate   B.4(23)
leaving   7.6.1(3)
left   7.6.1(3)
left curly bracket   2.1(15)
left parenthesis   2.1(15)
left square bracket   2.1(15)
Left_Angle_Quotation   A.3.3(21)
Left_Curly_Bracket   A.3.3(14)
Left_Parenthesis   A.3.3(8)
Left_Square_Bracket   A.3.3(12)
legal
   construct   1.1.2(27)
   partition   1.1.2(29)
legality determinable via semantic dependences   10(3)
legality rules   1.1.2(27)
length   A.4.4(9), A.4.5(6), B.4(34), B.4(39), B.4(44), F.3.3(11)
   of a dimension of an array   3.6(13)
   of a one-dimensional array   3.6(13)
Length attribute   3.6.2(9), K(117)
Length(N) attribute   3.6.2(10), K(115)
Length_Check   11.5(15)
   [partial]   4.5.1(8), 4.6(37), 4.6(52)
Length_Error   12.1(24)
Length_Range   A.4.4(8)
less than operator   4.4(1), 4.5.2(1)
less than or equal operator   4.4(1), 4.5.2(1)
less-than sign   2.1(15)
Less_Than_Sign   A.3.3(10)
letter
   a category of Character   A.3.2(24)
Letter_Set   A.4.6(4)
letter_or_digit   2.3(3)
   used   2.3(2), P(1)
Level   3.5.1(14)
   accessibility   3.10.2(3)
   library   3.10.2(22)
Level_1   3.10.2(22)
Level_1_Type   3.10.2(22)
Level_2   3.10.2(22)
lexical element   2.2(1)
lexicographic order   4.5.2(26)
LF   A.3.3(5), J.5(4)
Lib_Unit   3.10.2(22)
library   10.1.4(9)
   informal introduction   10(2)
library level   3.10.2(22)
library unit   10.1(3), 10.1.1(9), N(22)
   informal introduction   10(2)
   See also   language-defined library units
library unit pragma   10.1.5(7)
   All_Calls_Remote   E.2.3(6)
   categorization pragmas   E.2(2)
   Elaborate_Body   10.2.1(24)
   Preelaborate   10.2.1(4)
   Pure   10.2.1(15)
library_item   10.1.1(4)
   used   10.1.1(3), P(1)
   informal introduction   10(2)
library_unit_body   10.1.1(7)
   used   10.1.1(4), P(1)
library_unit_declaration   10.1.1(5)
   used   10.1.1(4), P(1)
library_unit_renaming_declaration   10.1.1(6)
   used   10.1.1(4), P(1)
lifetime   3.10.2(3)
Light   3.5.1(14)
Limit   3.3.1(33), 7.5(20)
limited type   7.5(1), 7.5(3), N(23)
   becoming nonlimited   7.3.1(5), 7.5(16)
Limited_Controlled   7.6(7)
Limited_Tagged   12.3(11)
Limited_Untagged   12.3(11)
line   2.2(2), 3.6(28), A.10.1(38)
line terminator   A.10(7)
Line_Length   A.10.1(25)
Line_Size   3.5.4(34)
Link   3.10.1(15), 12.5.4(8)
link name   B.1(35)
link-time error
   See post-compilation error   1.1.2(29), 1.1.5(4)
Linker_Options pragma   B.1(8), L(19)
linking
   See partition building   10.2(2)
List   7.3(24)
List pragma   2.8(21), L(20)
literal   3.9.1(13), 4.2(1)
   See also aggregate   4.3(1)
   based   2.4.2(1)
   decimal   2.4.1(1)
   numeric   2.4(1)
little endian   13.5.3(2)
load time   C.4(3)
Local   7.3(7), 9.3(20)
local to   8.1(14)
Local_Coordinate   3.4(37)
local_name   13.1(3)
   used   13.2(3), 13.3(2), 13.4(2), 13.5.1(2), 13.5.1(3), 13.11.3(3),
        B.1(5), B.1(6), B.1(7), C.5(3), C.6(3), C.6(4), C.6(5), C.6(6),
        E.4.1(3), L(3), L(4), L(5), L(7), L(8), L(9), L(13), L(14), L(24),
        L(38), L(39), P(1)
localization   3.5.2(4), 3.5.2(5)
Lock   D.12(9), D.12(10)
locking policy   D.3(6)
Locking_Policy pragma   D.3(3), L(21)
Log   A.5.1(4), G.1.2(3)
Logical   B.5(7)
logical operator   4.5.1(2)
   See also not operator   4.5.6(3)
logical_operator   4.5(2)
Long   4.9(43), B.3(7)
Long_Binary   B.4(10)
long_double   B.3(17)
Long_Float   3.5.7(15), 3.5.7(16), 3.5.7(17)
Long_Floating   B.4(9)
Long_Integer   3.5.4(22), 3.5.4(25), 3.5.4(28)
Look_Ahead   A.10.1(43)
loop parameter   5.5(6)
loop_parameter_specification   5.5(4)
   used   5.5(3), P(1)
loop_statement   5.5(2)
   used   5.1(5), P(1)
low line   2.1(15)
low-level programming   C(1)
Low_Limit   3.3.1(33)
Low_Line   A.3.3(12)
Low_Order_First   13.5.3(2), B.4(25)
lower bound
   of a range   3.5(4)
lower-case letter
   a category of Character   A.3.2(25)
lower_case_identifier_letter   2.1(9)
Lower_Case_Map   A.4.6(5)
Lower_Set   A.4.6(4)
LR(1)   1.1.4(14)

Machine attribute   A.5.3(60), K(119)
machine code insertion   13.8(1), C.1(2)
machine numbers
   of a floating point type   3.5.7(8)
Machine_Code   J.1(9)
   child of System   13.8(7)
Machine_Emax attribute   A.5.3(8), K(123)
Machine_Emin attribute   A.5.3(7), K(125)
Machine_Mantissa attribute   A.5.3(6), K(127)
Machine_Overflows attribute   A.5.3(12), A.5.4(4), K(129), K(131)
Machine_Radix attribute   A.5.3(2), A.5.4(2), K(133), K(135)
Machine_Radix clause   13.3(7), F.1(1)
Machine_Rounds attribute   A.5.3(11), A.5.4(3), K(137), K(139)
macro
   See generic unit   12(1)
Macron   A.3.3(21)
Main   3.9.2(20), 3.10.2(22), 6.3.1(21), 6.3.2(5), 7.3(7), 7.6.1(18),
        9.4(20), 10.1.1(33), 11.4.2(10), 13.11.3(6)
main subprogram
   for a partition   10.2(7)
Major   3.5.1(16)
Male   3.2.2(15)
malloc
   See allocator   4.8(1)
Maps
   child of Ada.Strings   A.4.2(3)
Mark_Release_Pool_Type   13.11(39)
marshalling   E.4(9)
Masculine_Ordinal_Indicator   A.3.3(22)
Mask   4.7(7)
Mass   3.5.7(21), 12.5(13)
master   7.6.1(3)
match
   a character to a pattern character   A.4.2(54)
   a character to a pattern character, with respect to a character mapping
        function   A.4.2(64)
   a string to a pattern string   A.4.2(54)
matching components   4.5.2(16)
Matrix   3.6(26)
Matrix_Rec   3.7(34)
Max   3.3.2(10)
Max attribute   3.5(19), K(141)
Max_Base_Digits   3.5.7(6), 13.7(8)
   named number in package System   13.7(8)
Max_Binary_Modulus   3.5.4(7), 13.7(7)
   named number in package System   13.7(7)
Max_Decimal_Digits   F.2(5)
Max_Delta   F.2(4)
Max_Digits   3.5.7(6), 13.7(8)
   named number in package System   13.7(8)
Max_Digits_Binary   B.4(11)
Max_Digits_Long_Binary   B.4(11)
Max_Image_Width   A.5.2(13), A.5.2(25)
Max_Int   3.5.4(14), 13.7(6)
   named number in package System   13.7(6)
Max_Length   A.4.4(5)
Max_Line_Size   3.3.2(10)
Max_Mantissa   13.7(9)
   named number in package System   13.7(9)
Max_Nonbinary_Modulus   3.5.4(7), 13.7(7)
   named number in package System   13.7(7)
Max_Scale   F.2(3)
Max_Size_In_Storage_Elements attribute   13.11.1(3), K(145)
maximum box error
   for a component of the result of evaluating a complex function   G.2.6(3)
maximum line length   A.10(11)
maximum page length   A.10(11)
maximum relative error
   for a component of the result of evaluating a complex function   G.2.6(3)
   for the evaluation of an elementary function   G.2.4(2)
Medium   13.3(81)
Mega   4.9(43)
Membership   A.4.1(6)
membership test   4.5.2(2)
Memory_Size   13.7(13)
mentioned in a with_clause   10.1.2(6)
message
   See dispatching call   3.9.2(1)
Message_Procedure   3.10(26)
method
   See dispatching subprogram   3.9.2(1)
methodological restriction   10.1.3(13)
metrics   1.1.2(35), C.3.1(15), C.7.2(20), D(2), D.5(13), D.6(4), D.8(37),
        D.9(9), D.12(6)
Micro_Sign   A.3.3(22)
Microseconds   D.8(14)
Middle_Dot   A.3.3(22)
Midweek   3.4(37)
Milliseconds   D.8(14)
Min attribute   3.5(16), K(147)
Min_Cell   6.1(39)
Min_Delta   F.2(4)
Min_Int   3.5.4(14), 13.7(6)
   named number in package System   13.7(6)
Min_Scale   F.2(3)
Minimum   8.5.4(21)
minus   2.1(15)
minus operator   4.4(1), 4.5.3(1), 4.5.4(1)
Mix   12.5.3(13)
Mix_Code   13.4(13)
Mixed   3.5.1(15)
mixed-language programs   B(1), C.1(4)
mod operator   4.4(1), 4.5.5(1)
mod_clause   J.8(1)
   used   13.5.1(2), P(1)
mode   6.1(16), 8.5(7), 13.5.1(26), A.8.1(9), A.8.4(9), A.10.1(12),
        A.12.1(11)
   used   6.1(15), 12.4(2), P(1)
mode conformance   6.3.1(16)
   required   8.5.4(4), 12.5.4(5), 12.6(7), 12.6(8)
mode of operation
   nonstandard   1.1.5(11)
   standard   1.1.5(11)
Mode_Error   A.8.1(15), A.8.4(18), A.10.1(85), A.12.1(26), A.13(4)
Mode_Mask   13.5.1(27)
Model attribute   A.5.3(68), G.2.2(7), K(151)
model interval   G.2.1(4)
   associated with a value   G.2.1(4)
model number   G.2.1(3)
model-oriented attributes
   of a floating point subtype   A.5.3(63)
Model_Emin attribute   A.5.3(65), G.2.2(4), K(155)
Model_Epsilon attribute   A.5.3(66), K(157)
Model_Mantissa attribute   A.5.3(64), G.2.2(3), K(159)
Model_Small attribute   A.5.3(67), K(161)
modular type   3.5.4(1)
modular_type_definition   3.5.4(4)
   used   3.5.4(2), P(1)
Modular_IO   A.10.1(57)
module
   See package   7(1)
modulus   G.1.1(9)
   of a modular type   3.5.4(7)
Modulus attribute   3.5.4(17), K(163)
Money   3.5.9(28), F.1(4)
Month   9.6(13)
Month_Number   9.6(11)
Move   6.2(12), A.4.3(7)
Msg_Type   13.13.2(40)
multi-dimensional array   3.6(12)
Multiplication_Sign   A.3.3(24)
multiply   2.1(15)
multiply operator   4.4(1), 4.5.5(1)
multiplying operator   4.5.5(1)
multiplying_operator   4.5(6)
   used   4.4(5), P(1)
mutable   3.7(28), 7.6(17)
MW   A.3.3(18)
My_Abstraction   10.1.1(35)
My_Controlled   13.11.3(6)
My_Controlled_Access   13.11.3(6)
My_Field_Size   3.9.3(3)
My_Int   7.3.1(7), 12.3(22), 13.9.1(12)
My_Read   13.3(84)
My_Type   10.1.1(35)
My_Write   8.5.4(14), 13.13.2(40)

N   4.9(37), 8.6(29)
n-dimensional array_aggregate   4.3.3(6)
NAK   A.3.3(6)
name   4.1(2), 13.7(4), 13.11.2(3), A.8.1(9), A.8.4(9), A.10.1(12),
        A.12.1(11)
   used   2.8(3), 3.2.2(4), 4.1(4), 4.1(5), 4.1(6), 4.4(7), 4.6(2), 5.2(2),
        5.7(2), 5.8(2), 6.3.2(3), 6.4(2), 6.4(3), 6.4(6), 8.4(3), 8.5.1(2),
        8.5.2(2), 8.5.3(2), 8.5.4(2), 8.5.5(2), 9.5.3(2), 9.5.4(2), 9.8(2),
        10.1.1(8), 10.1.2(4), 10.2.1(3), 10.2.1(14), 10.2.1(20), 10.2.1(21),
        10.2.1(22), 11.2(5), 11.3(2), 11.5(4), 12.3(2), 12.3(5), 12.6(4),
        12.7(2), 13.1(3), 13.3(2), C.3.1(2), C.3.1(4), E.2.1(3), E.2.2(3),
        E.2.3(3), E.2.3(5), H.3.2(3), L(2), L(6), L(10), L(11), L(12), L(15),
        L(16), L(17), L(26), L(28), L(30), L(31), L(34), L(36), P(1)
   [partial]   3.1(1)
   of (a view of) an entity   3.1(8)
   of a pragma   2.8(9)
   of an external file   A.7(1)
name resolution rules   1.1.2(26)
Name_Error   A.8.1(15), A.8.4(18), A.10.1(85), A.12.1(26), A.13(4)
Name_Server   E.4.2(3)
named association   6.4(7), 12.3(6)
named component association   4.3.1(6)
named discriminant association   3.7.1(4)
named entry index   9.5.2(21)
named number   3.3(24)
named type   3.2.1(7)
named_array_aggregate   4.3.3(4)
   used   4.3.3(2), P(1)
Names
   child of Ada.Interrupts   C.3.2(12)
names of special_characters   2.1(15)
Nanoseconds   D.8(14)
Native_Binary   B.4(25)
Natural   3.5.4(12), 3.5.4(13), A.1(13)
NBH   A.3.3(17)
needed
   of a compilation unit by another   10.2(2)
   remote call interface   E.2.3(18)
   shared passive library unit   E.2.1(11)
needed component
   extension_aggregate record_component_association_list   4.3.2(6)
   record_aggregate record_component_association_list   4.3.1(9)
NEL   A.3.3(17)
Nested   3.10.2(22), 7.3.1(7)
Nested_Type   3.10.2(22)
Network_Stream   13.13.2(40)
Network_IO   13.13.2(40)
new
   See allocator   4.8(1)
New_Char_Array   B.3.1(9)
New_Line   A.10.1(28)
New_Page   A.10.1(31)
New_String   B.3.1(10)
New_Tape   E.4.2(5)
Next   8.5.4(17), 12.3(22)
Next_Action   9.1(27)
Next_Frame   6.1(39)
Next_Lexeme   9.1(27)
Next_Work_Item   9.1(23)
Next_Id   3.6(11)
Ninety_Six   3.6.3(8)
No_Break_Space   A.3.3(21)
Node   12.5.4(8)
nominal subtype   3.3(23), 3.3.1(8)
   associated with a type_conversion   4.6(27)
   associated with a dereference   4.1(9)
   associated with an indexed_component   4.1.1(5)
   of a name   4.1(9)
   of a component   3.6(20)
   of a formal parameter   6.1(23)
   of a generic formal object   12.4(9)
   of a record component   3.8(14)
   of the result of a function_call   6.4(12)
non-normative
   See informative   1.1.2(18)
Non_Limited_Tagged   12.3(11)
Non_Limited_Untagged   12.3(11)
Non_Reentrant   13.11.3(6)
nondispatching call
   on a dispatching operation   3.9.2(1)
nonexistent   13.11.2(10), 13.11.2(16)
nongraphic character   3.5(32)
nonlimited type   7.5(7)
   becoming nonlimited   7.3.1(5), 7.5(16)
nonstandard integer type   3.5.4(26)
nonstandard mode   1.1.5(11)
nonstandard real type   3.5.6(8)
normal completion   7.6.1(2)
normal library unit   E.2(4)
normal state of an object   11.6(6), 13.9.1(4)
   [partial]   9.8(21), A.13(17)
normal termination
   of a partition   10.2(25)
Normalize_Scalars pragma   H.1(3), L(22)
normalized exponent   A.5.3(14)
normalized number   A.5.3(10)
normative   1.1.2(14)
not equal operator   4.4(1), 4.5.2(1)
not in (membership test)   4.4(1), 4.5.2(2)
not operator   4.4(1), 4.5.6(3)
Not_Sign   A.3.3(21)
notes   1.1.2(38)
notwithstanding   10.1.6(2), 10.2(18), B.1(22), B.1(38), C.3.1(19), E.2.1(8),
        E.2.1(11), E.2.3(18), J.3(6)
NT   3.4(38), 3.9.1(4)
NT2   3.9.1(4)
NUL   A.3.3(5), B.3(20), J.5(4)
null access value   4.2(9)
null array   3.6.1(7)
null constraint   3.2(7)
null pointer
   See null access value   4.2(9)
null range   3.5(4)
null record   3.8(15)
null slice   4.1.2(7)
null string literal   2.6(6)
null value
   of an access type   3.10(13)
Null_Address   13.7(12)
   constant in System   13.7(12)
Null_Bounded_String   A.4.4(7), A.4.4(106)
Null_Key   7.3.1(15), 7.4(13)
Null_Occurrence   11.4.1(3)
Null_Ptr   B.3.1(7)
Null_Set   A.4.2(5), A.4.7(5)
null_statement   5.1(6)
   used   5.1(4), P(1)
Null_Task_ID   C.7.1(2)
Null_Unbounded_String   A.4.5(5)
Null_Id   11.4.1(2)
Num   A.10.1(52), A.10.1(57), A.10.1(63), A.10.1(68), A.10.1(73), B.4(31),
        F.3.3(11)
number sign   2.1(15)
Number_Base   A.10.1(6), A.10.8(3)
number_declaration   3.3.2(2)
   used   3.1(3), P(1)
Number_Sign   A.3.3(8)
numeral   2.4.1(3)
   used   2.4.1(2), 2.4.1(4), 2.4.2(3), P(1)
Numeric   B.4(20)
numeric type   3.5(1)
Numeric_Error   J.6(2)
numeric_literal   2.4(2)
   used   4.4(7), P(1)
Numerics   G(1)
   child of Ada   A.5(3)

object   3.3(2), 13.7.2(2), 13.11.2(3), N(24)
   [partial]   3.2(1)
object-oriented programming (OOP)
   See dispatching operations of tagged types   3.9.2(1)
   See tagged types and type extensions   3.9(1)
object_declaration   3.3.1(2)
   used   3.1(3), P(1)
Object_Pointer   13.7.2(3)
object_renaming_declaration   8.5.1(2)
   used   8.5(2), P(1)
obsolescent feature   J(1)
occur immediately within   8.1(13)
occurrence (of an exception)   11(1)
occurrence
   of an interrupt   C.3(2)
octal
   literal   2.4.2(1)
octal literal   2.4.2(1)
On_Stacks   12.8(14)
On_Vectors   12.1(24), 12.2(9)
one's complement
   modular types   3.5.4(27)
one-dimensional array   3.6(12)
one-pass context_clauses   10.1.2(1)
One_Discrim   7.3(13)
only as a completion
   entry_body   9.5.2(16)
OOP (object-oriented programming)
   See dispatching operations of tagged types   3.9.2(1)
   See tagged types and type extensions   3.9(1)
Op_A   3.9.2(20)
Op_B   3.9.2(20)
Op1   7.3.1(7), 9.5(4)
Op2   7.3.1(7), 9.5(4)
opaque type
   See private types and private extensions   7.3(1)
Open   7.5(19), 7.5(20), 11.4.2(3), 11.4.2(6), A.8.1(7), A.8.4(7),
        A.10.1(10), A.12.1(9)
open alternative   9.7.1(14)
open entry   9.5.3(5)
   of a protected object   9.5.3(7)
   of a task   9.5.3(6)
operand
   of a type_conversion   4.6(3)
   of a qualified_expression   4.7(3)
operand interval   G.2.1(6)
operand type
   of a type_conversion   4.6(3)
operates on a type   3.2.3(1)
operation   3.2(10)
operator   6.6(1)
   &   4.4(1), 4.5.3(3)
   *   4.4(1), 4.5.5(1)
   **   4.4(1), 4.5.6(7)
   +   4.4(1), 4.5.3(1), 4.5.4(1)
   =   4.4(1), 4.5.2(1)
   -   4.4(1), 4.5.3(1), 4.5.4(1)
   /   4.4(1), 4.5.5(1)
   /=   4.4(1), 4.5.2(1)
   <   4.4(1), 4.5.2(1)
   <=   4.4(1), 4.5.2(1)
   >   4.4(1), 4.5.2(1)
   >=   4.4(1), 4.5.2(1)
   abs   4.4(1), 4.5.6(1)
   ampersand   4.4(1), 4.5.3(3)
   and   4.4(1), 4.5.1(2)
   binary   4.5(9)
   binary adding   4.5.3(1)
   concatenation   4.4(1), 4.5.3(3)
   divide   4.4(1), 4.5.5(1)
   equal   4.4(1), 4.5.2(1)
   equality   4.5.2(1)
   exponentiation   4.4(1), 4.5.6(7)
   greater than   4.4(1), 4.5.2(1)
   greater than or equal   4.4(1), 4.5.2(1)
   highest precedence   4.5.6(1)
   less than   4.4(1), 4.5.2(1)
   less than or equal   4.4(1), 4.5.2(1)
   logical   4.5.1(2)
   minus   4.4(1), 4.5.3(1), 4.5.4(1)
   mod   4.4(1), 4.5.5(1)
   multiply   4.4(1), 4.5.5(1)
   multiplying   4.5.5(1)
   not   4.4(1), 4.5.6(3)
   not equal   4.4(1), 4.5.2(1)
   or   4.4(1), 4.5.1(2)
   ordering   4.5.2(1)
   plus   4.4(1), 4.5.3(1), 4.5.4(1)
   predefined   4.5(9)
   relational   4.5.2(1)
   rem   4.4(1), 4.5.5(1)
   times   4.4(1), 4.5.5(1)
   unary   4.5(9)
   unary adding   4.5.4(1)
   user-defined   6.6(1)
   xor   4.4(1), 4.5.1(2)
operator precedence   4.5(1)
operator_symbol   6.1(9)
   used   4.1(3), 4.1.3(3), 6.1(5), 6.1(11), P(1)
optimization   11.5(29), 11.6(1)
Optimize pragma   2.8(23), L(23)
Option   12.5.3(13)
or else (short-circuit control form)   4.4(1), 4.5.1(1)
or operator   4.4(1), 4.5.1(2)
ordering operator   4.5.2(1)
ordinary fixed point type   3.5.9(1), 3.5.9(8)
ordinary_fixed_point_definition   3.5.9(3)
   used   3.5.9(2), P(1)
Origin   3.9.1(12)
OSC   A.3.3(19)
other_control_function   2.1(14)
   used   2.1(2), P(1)
Other_Procedure   3.10(26)
others choice   4.3.3(6)
Outer   13.14(19)
output   A.6(1)
Output attribute   13.13.2(19), 13.13.2(29), K(165), K(169)
Output clause   13.3(7), 13.13.2(36)
overall interpretation
   of a complete context   8.6(10)
Overflow_Check   11.5(16)
   [partial]   3.5.4(20), 4.4(11), 5.4(13), G.2.1(11), G.2.2(7), G.2.3(25),
        G.2.4(2), G.2.6(3)
overload resolution   8.6(1)
overloadable   8.3(7)
overloaded   8.3(6)
   enumeration literal   3.5.1(9)
overloading rules   1.1.2(26), 8.6(2)
override   8.3(9), 12.3(17)
   a primitive subprogram   3.2.3(7)
Overwrite   A.4.3(27), A.4.3(28), A.4.4(62), A.4.4(63), A.4.5(57), A.4.5(58)

P   3.4(34), 3.4(38), 3.9.1(4), 3.9.3(3), 3.9.3(16), 3.10(9), 3.10.2(22),
        7.3(7), 7.3(9), 7.3(13), 7.3.1(7), 7.5(2), 8.2(3), 8.3(26), 8.4(7),
        8.5.4(8), 9.2(11), 10.1.1(9), 12.3(18), 12.3(22), 12.5.3(11),
        12.5.4(8), 13.11.3(6), 13.14(1), 13.14(13)
P.Q   7.3.1(7), 8.2(3), 8.3(26)
P1   3.9.2(20), 5.2(4), 7.3(7), 13.1(14), 13.14(10)
P10   11.6(5)
P2   3.9.2(20), 5.2(4), 7.3(7), 13.1(14), 13.14(10)
Pack   3.9.3(10), 3.10.1(23)
Pack pragma   13.2(3), L(24)
Pack.Child   3.10.1(23)
Pack1   3.9.3(6)
Pack2   3.9.3(6)
Pack3   3.9.3(6)
Package   7(1), N(25)
package instance   12.3(13)
package-private extension   7.3(14)
package-private type   7.3(14)
package_body   7.2(2)
   used   3.11(6), 10.1.1(7), P(1)
package_body_stub   10.1.3(4)
   used   10.1.3(2), P(1)
package_declaration   7.1(2)
   used   3.1(3), 10.1.1(5), P(1)
package_renaming_declaration   8.5.3(2)
   used   8.5(2), 10.1.1(6), P(1)
package_specification   7.1(3)
   used   7.1(2), 12.1(4), P(1)
packed   13.2(5)
Packed_Decimal   B.4(12)
Packed_Descriptor   13.6(6)
Packed_Format   B.4(26)
Packed_Signed   B.4(27)
Packed_Unsigned   B.4(27)
packing
   aspect of representation   13.2(5)
padding bits   13.1(7)
Page   13.3(80), A.10.1(39)
Page pragma   2.8(22), L(25)
page terminator   A.10(7)
Page_Length   A.10.1(26)
Page_Num   3.5.4(34)
Painted_Point   3.9.1(11)
Pair   6.4(20)
parallel processing
   See task   9(1)
Parallel_Simulation   A.5.2(60)
parameter
   See also discriminant   3.7(1)
   See also loop parameter   5.5(6)
   See formal parameter   6.1(17)
   See generic formal parameter   12(1)
parameter assigning back   6.4.1(17)
parameter copy back   6.4.1(17)
parameter mode   6.1(18)
parameter passing   6.4.1(1)
parameter_and_result_profile   6.1(13)
   used   3.10(5), 6.1(4), P(1)
parameter_association   6.4(5)
   used   6.4(4), P(1)
parameter_profile   6.1(12)
   used   3.10(5), 6.1(4), 9.5.2(2), 9.5.2(3), 9.5.2(6), P(1)
parameter_specification   6.1(15)
   used   6.1(14), P(1)
Parameterless_Handler   C.3.2(2)
Params_Stream_Type   E.5(6)
Parent   7.3(7), 7.3.1(7), 8.4(7), 10.1.3(20), 10.1.3(21), 10.1.3(23),
        12.3(11)
parent body
   of a subunit   10.1.3(8)
parent declaration
   of a library_item   10.1.1(10)
   of a library unit   10.1.1(10)
parent subtype   3.4(3)
parent type   3.4(3)
parent unit
   of a library unit   10.1.1(10)
Parent.Child   7.3.1(7), 8.4(7)
parent_unit_name   10.1.1(8)
   used   6.1(5), 6.1(7), 7.1(3), 7.2(2), 10.1.3(7), P(1)
Parser   9.1(27)
part
   of an object or value   3.2(6)
partial view
   of a type   7.3(4)
Partition   10(1), 10.2(2), N(26)
partition building   10.2(2)
partition communication subsystem (PCS)   E.5(1)
Partition_Check
   [partial]   E.4(19)
Partition_ID   E.5(4)
Partition_ID attribute   E.1(9), K(173)
pass by copy   6.2(2)
pass by reference   6.2(2)
passive partition   E.1(2)
PC-map approach to finalization   7.6.1(24)
PCS (partition communication subsystem)   E.5(1)
pending interrupt occurrence   C.3(2)
per-object constraint   3.8(18)
per-object expression   3.8(18)
Percent   J.5(6)
Percent_Sign   A.3.3(8)
perfect result set   G.2.3(5)
periodic task
   See delay_until_statement   9.6(39)
   example   9.6(39)
Peripheral   3.8.1(25)
Peripheral_Ref   3.10(22)
Person   3.10.1(19), 3.10.1(22)
Person_Name   3.10.1(20)
Pi   A.5(3)
Pic_String   F.3.3(7)
Picture   F.3.3(4)
picture String
   for edited output   F.3.1(1)
Picture_Error   F.3.3(9)
Pilcrow_Sign   A.3.3(22)
plain_char   B.3(11)
PLD   A.3.3(17)
PLU   A.3.3(17)
plus operator   4.4(1), 4.5.3(1), 4.5.4(1)
plus sign   2.1(15)
Plus_Minus_Sign   A.3.3(22)
Plus_Sign   A.3.3(8)
PM   A.3.3(19)
PO   9.4(20)
point   2.1(15), 3.9(32)
pointer   B.3.2(5)
   See access value   3.10(1)
   See type System.Address   13.7(34)
pointer type
   See access type   3.10(1)
Pointer_Error   B.3.2(8)
Pointers
   child of Interfaces.C   B.3.2(4)
polymorphism   3.9(1), 3.9.2(1)
pool element   3.10(7), 13.11(11)
pool type   13.11(11)
pool-specific access type   3.10(7), 3.10(8)
Pool_Ptr   13.14(13)
Pop   12.8(3), 12.8(7), 12.8(14)
Pos attribute   3.5.5(2), K(175)
position   13.5.1(4)
   used   13.5.1(3), P(1)
Position attribute   13.5.2(2), K(179)
position number   3.5(1)
   of an enumeration value   3.5.1(7)
   of an integer value   3.5.4(15)
positional association   6.4(7), 12.3(6)
positional component association   4.3.1(6)
positional discriminant association   3.7.1(4)
positional_array_aggregate   4.3.3(3)
   used   4.3.3(2), P(1)
Positive   3.5.4(12), 3.5.4(13), 3.6.3(3), A.1(13)
Positive_Count   A.8.4(4), A.10(10), A.10.1(5), A.12.1(7)
POSIX   1.2(8)
possible interpretation   8.6(14)
   for direct_names   8.3(24)
   for selector_names   8.3(24)
post-compilation error   1.1.2(29)
post-compilation rules   1.1.2(29), 10.1.3(15), 10.1.5(8), 10.2(2), 12.3(19),
        13.12(8), D.2.2(4), D.3(5), D.4(5), E(2), E.1(2), E.2.1(10),
        E.2.3(17), H.1(4), H.3.1(4)
potentially blocking operation   9.5.1(8)
   Abort_Task   C.7.1(16)
   delay_statement   9.6(34), D.9(5)
   remote subprogram call   E.4(17)
   RPC operations   E.5(23)
   Suspend_Until_True   D.10(10)
potentially use-visible   8.4(8)
Pound_Sign   A.3.3(21)
Power_16   3.3.2(10)
Pragma   2.8(1), 2.8(2), L(1), N(27)
pragma argument   2.8(9)
pragma name   2.8(9)
pragma, categorization   E.2(2)
   Remote_Call_Interface   E.2.3(2)
   Remote_Types   E.2.2(2)
   Shared_Passive   E.2.1(2)
pragma, configuration   10.1.5(8)
   Locking_Policy   D.3(5)
   Normalize_Scalars   H.1(4)
   Queuing_Policy   D.4(5)
   Restrictions   13.12(8)
   Reviewable   H.3.1(4)
   Suppress   11.5(5)
   Task_Dispatching_Policy   D.2.2(4)
pragma, identifier specific to   2.8(10)
pragma, interfacing
   Convention   B.1(4)
   Export   B.1(4)
   Import   B.1(4)
   Linker_Options   B.1(4)
pragma, library unit   10.1.5(7)
   All_Calls_Remote   E.2.3(6)
   categorization pragmas   E.2(2)
   Elaborate_Body   10.2.1(24)
   Preelaborate   10.2.1(4)
   Pure   10.2.1(15)
pragma, program unit   10.1.5(2)
   Convention   B.1(29)
   Export   B.1(29)
   Import   B.1(29)
   Inline   6.3.2(2)
   library unit pragmas   10.1.5(7)
pragma, representation   13.1(1)
   Asynchronous   E.4.1(8)
   Atomic   C.6(14)
   Atomic_Components   C.6(14)
   Controlled   13.11.3(5)
   Convention   B.1(28)
   Discard_Names   C.5(6)
   Export   B.1(28)
   Import   B.1(28)
   Pack   13.2(5)
   Volatile   C.6(14)
   Volatile_Components   C.6(14)
pragma_argument_association   2.8(3)
   used   2.8(2), P(1)
pragmas
   All_Calls_Remote   E.2.3(5), L(2)
   Asynchronous   E.4.1(3), L(3)
   Atomic   C.6(3), L(4)
   Atomic_Components   C.6(5), L(5)
   Attach_Handler   C.3.1(4), L(6)
   Controlled   13.11.3(3), L(7)
   Convention   B.1(7), L(8)
   Discard_Names   C.5(3), L(9)
   Elaborate   10.2.1(20), L(10)
   Elaborate_All   10.2.1(21), L(11)
   Elaborate_Body   10.2.1(22), L(12)
   Export   B.1(6), L(13)
   Import   B.1(5), L(14)
   Inline   6.3.2(3), L(15)
   Inspection_Point   H.3.2(3), L(16)
   Interrupt_Handler   C.3.1(2), L(17)
   Interrupt_Priority   D.1(5), L(18)
   Linker_Options   B.1(8), L(19)
   List   2.8(21), L(20)
   Locking_Policy   D.3(3), L(21)
   Normalize_Scalars   H.1(3), L(22)
   Optimize   2.8(23), L(23)
   Pack   13.2(3), L(24)
   Page   2.8(22), L(25)
   Preelaborate   10.2.1(3), L(26)
   Priority   D.1(3), L(27)
   Pure   10.2.1(14), L(28)
   Queuing_Policy   D.4(3), L(29)
   Remote_Call_Interface   E.2.3(3), L(30)
   Remote_Types   E.2.2(3), L(31)
   Restrictions   13.12(3), L(32)
   Reviewable   H.3.1(3), L(33)
   Shared_Passive   E.2.1(3), L(34)
   Storage_Size   13.3(63), L(35)
   Suppress   11.5(4), L(36)
   Task_Dispatching_Policy   D.2.2(2), L(37)
   Volatile   C.6(4), L(38)
   Volatile_Components   C.6(6), L(39)
precedence of operators   4.5(1)
Pred attribute   3.5(25), K(181)
predefined environment   A(1)
predefined exception   11.1(4)
predefined library unit
   See   language-defined library units
predefined operation
   of a type   3.2.3(1)
predefined operations
   of a discrete type   3.5.5(10)
   of a fixed point type   3.5.10(17)
   of a floating point type   3.5.8(3)
   of a record type   3.8(24)
   of an access type   3.10.2(34)
   of an array type   3.6.2(15)
predefined operator   4.5(9)
   [partial]   3.2.1(9)
predefined type   3.2.1(10)
   See   language-defined types
Predefined_Equal   8.5.4(8)
preelaborable
   of an elaborable construct   10.2.1(5)
Preelaborate pragma   10.2.1(3), L(26)
preelaborated   10.2.1(11)
   [partial]   10.2.1(11), E.2.1(9)
preempted task   D.2.1(7)
preemptible resource   D.2.1(7)
preference
   for root numeric operators and ranges   8.6(29)
preference control
   See requeue   9.5.4(1)
prefix   4.1(4)
   used   4.1.1(2), 4.1.2(2), 4.1.3(2), 4.1.4(2), 4.1.4(4), 6.4(2), 6.4(3),
        P(1)
prescribed result
   for the evaluation of a complex arithmetic operation   G.1.1(42)
   for the evaluation of a complex elementary function   G.1.2(35)
   for the evaluation of an elementary function   A.5.1(37)
Pri   3.10.1(23)
primary   4.4(7)
   used   4.4(6), P(1)
primitive function   A.5.3(17)
primitive operation
   [partial]   3.2(1)
primitive operations   3.2.3(1), N(28)
   of a type   3.2.3(1)
primitive operator
   of a type   3.2.3(8)
primitive subprograms
   of a type   3.2.3(2)
Print   3.9.3(3), 6.4.1(5)
Print_Header   6.1(42)
Priority   13.7(16), D.1(10), D.1(15)
priority inheritance   D.1(15)
priority inversion   D.2.2(14)
priority of an entry call   D.4(9)
Priority pragma   D.1(3), L(27)
private declaration of a library unit   10.1.1(12)
private descendant
   of a library unit   10.1.1(12)
Private extension   3.2(2), 3.2(4), 3.9(2), 3.9.1(1), N(29)
   [partial]   7.3(14)
private library unit   10.1.1(12)
private operations   7.3.1(1)
private part   8.2(5)
   of a package   7.1(6), 12.3(12)
   of a protected unit   9.4(11)
   of a task unit   9.1(9)
Private type   3.2(2), 3.2(4), N(30)
   [partial]   7.3(14)
private types and private extensions   7.3(1)
private_extension_declaration   7.3(3)
   used   3.2.1(2), P(1)
private_type_declaration   7.3(2)
   used   3.2.1(2), P(1)
Probability   3.5.7(22)
procedure   6(1)
procedure instance   12.3(13)
procedure_call_statement   6.4(2)
   used   5.1(4), P(1)
processing node   E(2)
Producer   9.11(2), 9.11(3)
profile   6.1(22)
   associated with a dereference   4.1(10)
   fully conformant   6.3.1(18)
   mode conformant   6.3.1(16)
   subtype conformant   6.3.1(17)
   type conformant   6.3.1(15)
profile resolution rule
   name with a given expected profile   8.6(26)
Prog   B.4(107)
Program   10(1), 10.2(1), N(32)
program execution   10.2(1)
program library
   See library   10(2), 10.1.4(9)
Program unit   10.1(1), N(31)
program unit pragma   10.1.5(2)
   Convention   B.1(29)
   Export   B.1(29)
   Import   B.1(29)
   Inline   6.3.2(2)
   library unit pragmas   10.1.5(7)
program-counter-map approach to finalization   7.6.1(24)
Program_Error   A.1(46)
   raised by failure of run-time check   1.1.3(17), 1.1.3(20), 1.1.5(8),
        1.1.5(12), 3.5(32), 3.5.5(8), 3.10.2(29), 3.11(14), 4.6(57), 6.2(12),
        6.4(11), 6.5(20), 7.6.1(15), 7.6.1(16), 7.6.1(17), 7.6.1(18),
        7.6.1(20), 9.4(20), 9.5.1(17), 9.5.3(7), 9.7.1(21), 9.8(20),
        10.2(26), 11.1(4), 11.5(8), 11.5(19), 13.7.1(16), 13.9.1(9),
        13.11.2(13), 13.11.2(14), A.7(14), C.3.1(10), C.3.1(11), C.3.2(17),
        C.3.2(20), C.3.2(21), C.3.2(22), C.7.1(15), C.7.1(17), C.7.2(13),
        D.3(13), D.5(9), D.5(11), D.10(10), D.11(8), E.1(10), E.3(6),
        E.4(18), J.7.1(7)
Program_Status_Word   13.5.1(28)
propagate   11.4(1)
   an exception by a construct   11.4(6)
   an exception by an execution   11.4(6)
   an exception occurrence by an execution, to a dynamically enclosing
        execution   11.4(6)
proper_body   3.11(6)
   used   3.11(5), 10.1.3(7), P(1)
protected action   9.5.1(4)
   complete   9.5.1(6)
   start   9.5.1(5)
protected calling convention   6.3.1(12)
protected declaration   9.4(1)
protected entry   9.4(1)
protected function   9.5.1(1)
protected object   9(3), 9.4(1)
protected operation   9.4(1)
protected procedure   9.5.1(1)
protected subprogram   9.4(1), 9.5.1(1)
Protected type   3.2(2), N(33)
protected unit   9.4(1)
protected_body   9.4(7)
   used   3.11(6), P(1)
protected_body_stub   10.1.3(6)
   used   10.1.3(2), P(1)
protected_definition   9.4(4)
   used   9.4(2), 9.4(3), P(1)
protected_element_declaration   9.4(6)
   used   9.4(4), P(1)
protected_operation_declaration   9.4(5)
   used   9.4(4), 9.4(6), P(1)
protected_operation_item   9.4(8)
   used   9.4(7), P(1)
protected_type_declaration   9.4(2)
   used   3.2.1(3), P(1)
Pt   9.5(4)
ptrdiff_t   B.3(12)
PU1   A.3.3(18)
PU2   A.3.3(18)
public declaration of a library unit   10.1.1(12)
public descendant
   of a library unit   10.1.1(12)
public library unit   10.1.1(12)
Public_Part   3.9.3(16)
pure   10.2.1(16)
Pure pragma   10.2.1(14), L(28)
Push   6.3(9), 12.8(3), 12.8(6), 12.8(14)
Put   6.3.2(5), 6.4(26), 10.1.1(30), A.10.1(42), A.10.1(48), A.10.1(55),
        A.10.1(60), A.10.1(66), A.10.1(67), A.10.1(71), A.10.1(72),
        A.10.1(76), A.10.1(77), A.10.1(82), A.10.1(83), F.3.3(14), F.3.3(15),
        F.3.3(16), G.1.3(7), G.1.3(8)
Put_Item   12.6(22)
Put_Line   A.10.1(50)
Put_List   12.6(24)

Q   3.9.1(4), 3.9.3(3), 3.10.2(22), 7.3(7), 7.5(2), 8.2(12), 8.5.4(8),
        12.3(18), 13.1(14)
qualified_expression   4.7(2)
   used   4.4(7), 4.8(2), 13.8(2), P(1)
Query   J.5(6)
Question   3.6.3(7), A.3.3(10)
queuing policy   D.4(1), D.4(6)
Queuing_Policy pragma   D.4(3), L(29)
Quotation   A.3.3(8)
quotation mark   2.1(15)
quoted string
   See string_literal   2.6(1)
Quotient_Type   F.2(6)

R   3.3.1(20), 3.10.2(22), 7.3.1(7), 7.5(2), 8.2(3), 8.2(12), 12.5.3(15),
        12.5.4(13), 13.14(19)
R_Brace   J.5(6)
R_Bracket   J.5(6)
R2   7.5(2)
Rad_To_Deg   4.9(44)
Rainbow   3.2.2(15), 3.5.1(16)
raise
   an exception   11(1), 11.3(4), N(18)
   an exception occurrence   11.4(3)
Raise_Exception   11.4.1(4)
raise_statement   11.3(2)
   used   5.1(4), P(1)
Random   6.1(38), A.5.2(8), A.5.2(20)
random number   A.5.2(1)
Random_Coin   A.5.2(58)
Random_Die   A.5.2(56)
range   3.5(3), 3.5(4)
   used   3.5(2), 3.6(6), 3.6.1(3), 4.4(3), P(1)
   of a scalar subtype   3.5(7)
Range attribute   3.5(14), 3.6.2(7), K(187), K(189)
Range(N) attribute   3.6.2(8), K(185)
range_attribute_designator   4.1.4(5)
   used   4.1.4(4), P(1)
range_attribute_reference   4.1.4(4)
   used   3.5(3), P(1)
Range_Check   11.5(17)
   [partial]   3.2.2(11), 3.5(24), 3.5(27), 3.5(43), 3.5(44), 3.5(51),
        3.5(55), 3.5.5(7), 3.5.9(19), 4.2(11), 4.3.3(28), 4.5.1(8), 4.5.6(6),
        4.5.6(13), 4.6(28), 4.6(38), 4.6(46), 4.6(51), 4.7(4), 13.13.2(35),
        A.5.2(39), A.5.2(40), A.5.3(26), A.5.3(29), A.5.3(50), A.5.3(53),
        A.5.3(59), A.5.3(62), K(11), K(41), K(47), K(114), K(122), K(184),
        K(220), K(241)
range_constraint   3.5(2)
   used   3.2.2(6), 3.5.9(5), J.3(2), P(1)
Rank   12.5(16), B.5(31)
Rational   7.1(13)
Rational_Numbers   7.1(12), 7.2(10), 10.1.1(32)
Rational_Numbers.Reduce   10.1.1(31)
Rational_Numbers.IO   10.1.1(30)
Rational_IO   10.1.1(34)
RCI
   generic   E.2.3(7)
   library unit   E.2.3(7)
   package   E.2.3(7)
Re   G.1.1(6)
re-raise statement   11.3(3)
read   7.5(19), 7.5(20), 9.1(24), 9.5.2(33), 9.11(8), 9.11(10), 11.4.2(4),
        11.4.2(7), 13.13.1(5), 13.13.2(40), A.8.1(12), A.8.4(12), A.9(6),
        A.12.1(15), A.12.1(16), D.12(9), D.12(10), E.5(7)
   the value of an object   3.3(14)
Read attribute   13.13.2(6), 13.13.2(14), K(191), K(195)
Read clause   13.3(7), 13.13.2(36)
ready
   a task state   9(10)
ready queue   D.2.1(5)
ready task   D.2.1(5)
Real   3.5.7(21), B.5(6), G.1.1(2)
real literal   2.4(1)
real literals   3.5.6(4)
real time   D.8(18)
Real type   3.2(2), 3.2(3), 3.5.6(1), N(34)
real-time systems   C(1), D(1)
Real_Plus   8.5.4(15)
real_range_specification   3.5.7(3)
   used   3.5.7(2), 3.5.9(3), 3.5.9(4), P(1)
Real_Time
   child of Ada   D.8(3)
real_type_definition   3.5.6(2)
   used   3.2.1(4), P(1)
Real_IO   A.10.9(41)
Rec   3.10.2(22)
Rec_Ptr   3.10.2(22)
Receive   13.13.2(40)
receiving stub   E.4(10)
reclamation of storage   13.11.2(1)
recommended level of support   13.1(20)
   enumeration_representation_clause   13.4(9)
   record_representation_clause   13.5.1(17)
   Address attribute   13.3(15)
   Alignment attribute for objects   13.3(33)
   Alignment attribute for subtypes   13.3(29)
   bit ordering   13.5.3(7)
   Component_Size attribute   13.3(71)
   pragma Pack   13.2(7)
   required in Systems Programming Annex   C.2(2)
   Size attribute   13.3(42), 13.3(54)
   unchecked conversion   13.9(16)
   with respect to nonstatic expressions   13.1(21)
record   3.8(1)
Record extension   3.2(2), 3.4(5), 3.9.1(1), N(35)
record layout
   aspect of representation   13.5(1)
Record type   3.2(2), 3.8(1), N(36)
record_aggregate   4.3.1(2)
   used   4.3(2), 13.8(14), P(1)
record_component_association   4.3.1(4)
   used   4.3.1(3), P(1)
record_component_association_list   4.3.1(3)
   used   4.3.1(2), 4.3.2(2), P(1)
record_definition   3.8(3)
   used   3.8(2), 3.9.1(2), P(1)
record_extension_part   3.9.1(2)
   used   3.4(2), P(1)
record_representation_clause   13.5.1(2)
   used   13.1(2), P(1)
record_type_definition   3.8(2)
   used   3.2.1(4), P(1)
Red_Blue   3.2.2(15)
Reference   C.3.2(10), C.7.2(5)
reference parameter passing   6.2(2)
references   1.2(1)
Register   E.4.2(3)
Registered_Trade_Mark_Sign   A.3.3(21)
Reinitialize   C.7.2(6)
relation   4.4(3)
   used   4.4(2), P(1)
relational operator   4.5.2(1)
relational_operator   4.5(3)
   used   4.4(3), P(1)
relaxed mode   G.2(1)
Release   9.4(27), 9.4(29)
   execution resource associated with protected object   9.5.1(6)
rem operator   4.4(1), 4.5.5(1)
Remainder attribute   A.5.3(45), K(199)
Remainder_Type   F.2(6)
remote access   E.1(5)
remote access type   E.2.2(8)
remote access-to-class-wide type   E.2.2(8)
remote access-to-subprogram type   E.2.2(8)
remote call interface   E.2(4), E.2.3(7)
remote procedure call
   asynchronous   E.4.1(9)
remote subprogram   E.2.3(7)
remote subprogram binding   E.4(1)
remote subprogram call   E.4(1)
remote types library unit   E.2(4), E.2.2(4)
Remote_Call_Interface pragma   E.2.3(3), L(30)
Remote_Types pragma   E.2.2(3), L(31)
Remove   E.4.2(3)
renamed entity   8.5(3)
renamed view   8.5(3)
renaming-as-body   8.5.4(1)
renaming-as-declaration   8.5.4(1)
renaming_declaration   8.5(2)
   used   3.1(3), P(1)
rendezvous   9.5.2(25)
Replace_Element   A.4.4(27), A.4.5(21)
Replace_Slice   A.4.3(23), A.4.3(24), A.4.4(58), A.4.4(59), A.4.5(53),
        A.4.5(54)
Replicate   A.4.4(78), A.4.4(79), A.4.4(80)
representation
   change of   13.6(1)
representation aspect   13.1(8)
representation attribute   13.3(1)
representation item   13.1(1)
representation of an object   13.1(7)
representation pragma   13.1(1)
   Asynchronous   E.4.1(8)
   Atomic   C.6(14)
   Atomic_Components   C.6(14)
   Controlled   13.11.3(5)
   Convention   B.1(28)
   Discard_Names   C.5(6)
   Export   B.1(28)
   Import   B.1(28)
   Pack   13.2(5)
   Volatile   C.6(14)
   Volatile_Components   C.6(14)
representation-oriented attributes
   of a fixed point subtype   A.5.4(1)
   of a floating point subtype   A.5.3(1)
representation_clause   13.1(2)
   used   3.8(5), 3.11(4), 9.1(5), 9.4(5), 9.4(8), P(1)
represented in canonical form   A.5.3(10)
Request   9.1(26), 9.5.2(33)
requested decimal precision
   of a floating point type   3.5.7(4)
requeue   9.5.4(1)
requeue-with-abort   9.5.4(13)
requeue_statement   9.5.4(2)
   used   5.1(4), P(1)
requires a completion   3.11.1(1), 3.11.1(6)
   incomplete_type_declaration   3.10.1(3)
   protected_declaration   9.4(10)
   task_declaration   9.1(8)
   generic_package_declaration   7.1(5)
   generic_subprogram_declaration   6.1(20)
   package_declaration   7.1(5)
   subprogram_declaration   6.1(20)
   declaration of a partial view   7.3(4)
   declaration to which a pragma Elaborate_Body applies   10.2.1(25)
   deferred constant declaration   7.4(2)
   library_unit_declaration   10.2(18)
   protected entry_declaration   9.5.2(16)
Reraise_Occurrence   11.4.1(4), 11.4.1(19)
reserved interrupt   C.3(2)
reserved word   2.9(2)
Reserved_128   A.3.3(17)
Reserved_129   A.3.3(17)
Reserved_132   A.3.3(17)
Reserved_153   A.3.3(19)
Reserved_Check
   [partial]   C.3.1(10)
Reset   A.5.2(9), A.5.2(12), A.5.2(21), A.5.2(24), A.8.1(8), A.8.4(8),
        A.10.1(11), A.12.1(10)
resolution rules   1.1.2(26)
resolve
   overload resolution   8.6(14)
Resource   9.4(27), 9.4(28)
restriction   13.12(4)
   used   13.12(3), L(32)
Restrictions
   Immediate_Reclamation   H.4(10)
   Max_Asynchronous_Select_Nesting   D.7(18)
   Max_Protected_Entries   D.7(14)
   Max_Select_Alternatives   D.7(12)
   Max_Storage_At_Blocking   D.7(17)
   Max_Task_Entries   D.7(13)
   Max_Tasks   D.7(19)
   No_Abort_Statements   D.7(5)
   No_Access_Subprograms   H.4(17)
   No_Allocators   H.4(7)
   No_Asynchronous_Control   D.7(10)
   No_Delay   H.4(21)
   No_Dispatch   H.4(19)
   No_Dynamic_Priorities   D.7(9)
   No_Exceptions   H.4(12)
   No_Fixed_Point   H.4(15)
   No_Floating_Point   H.4(14)
   No_Implicit_Heap_Allocations   D.7(8)
   No_Local_Allocators   H.4(8)
   No_Nested_Finalization   D.7(4)
   No_Protected_Types   H.4(5)
   No_Recursion   H.4(22)
   No_Reentrancy   H.4(23)
   No_Task_Allocators   D.7(7)
   No_Task_Hierarchy   D.7(3)
   No_Terminate_Alternatives   D.7(6)
   No_Unchecked_Access   H.4(18)
   No_Unchecked_Conversion   H.4(16)
   No_Unchecked_Deallocation   H.4(9)
   No_IO   H.4(20)
Restrictions pragma   13.12(3), L(32)
result interval
   for a component of the result of evaluating a complex function   G.2.6(3)
   for the evaluation of a predefined arithmetic operation   G.2.1(8)
   for the evaluation of an elementary function   G.2.4(2)
result subtype
   of a function   6.5(3)
Result_Subtype   A.5.2(17)
return expression   6.5(3)
return-by-reference type   6.5(11)
return_statement   6.5(2)
   used   5.1(4), P(1)
Reverse_Solidus   A.3.3(12)
Reviewable pragma   H.3.1(3), L(33)
Rewind   E.4.2(2), E.4.2(5)
RI   A.3.3(17)
right curly bracket   2.1(15)
right parenthesis   2.1(15)
right square bracket   2.1(15)
Right_Angle_Quotation   A.3.3(22)
Right_Curly_Bracket   A.3.3(14)
Right_Indent   6.1(37)
Right_Parenthesis   A.3.3(8)
Right_Square_Bracket   A.3.3(12)
Roman   3.6(26)
Roman_Digit   3.5.2(9)
Root   7.3.1(7)
root library unit   10.1.1(10)
root type
   of a class   3.4.1(2)
root_integer   3.5.4(14)
   [partial]   3.4.1(8)
root_real   3.5.6(3)
   [partial]   3.4.1(8)
Root_Storage_Pool   13.11(6)
Root_Stream_Type   13.13.1(3)
rooted at a type   3.4.1(2)
Rosso   8.5.4(16)
Rot   8.5.4(16)
rotate   B.2(9)
Rotate_Left   B.2(6)
Rotate_Right   B.2(6)
Rouge   8.5.4(16)
Round attribute   3.5.10(12), K(203)
Rounding attribute   A.5.3(36), K(207)
Row   12.1(19)
RPC
   child of System   E.5(3)
RPC-receiver   E.5(21)
RPC_Receiver   E.5(11)
RS   A.3.3(6), J.5(4)
run-time check
   See language-defined check   11.5(2)
run-time error   1.1.2(30), 1.1.5(6), 11.5(2), 11.6(1)
run-time polymorphism   3.9.2(1)
run-time semantics   1.1.2(30)
run-time type
   See tag   3.9(3)
running a program
   See program execution   10.2(1)
running task   D.2.1(6)

S   5.4(18), 13.1(7), 13.3(48), 13.14(19)
S'Adjacent   A.5.3(49), K(10)
S'Ceiling   A.5.3(34), K(29)
S'Class'Input   13.13.2(33), K(94)
S'Class'Output   13.13.2(30), K(167)
S'Class'Read   13.13.2(15), K(193)
S'Class'Write   13.13.2(12), K(284)
S'Compose   A.5.3(25), K(40)
S'Copy_Sign   A.5.3(52), K(46)
S'Exponent   A.5.3(19), K(62)
S'Floor   A.5.3(31), K(76)
S'Fraction   A.5.3(22), K(82)
S'Input   13.13.2(23), K(98)
S'Leading_Part   A.5.3(55), K(110)
S'Machine   A.5.3(61), K(121)
S'Model   A.5.3(69), K(153)
S'Output   13.13.2(20), K(171)
S'Read   13.13.2(7), K(197)
S'Remainder   A.5.3(46), K(201)
S'Rounding   A.5.3(37), K(209)
S'Scaling   A.5.3(28), K(219)
S'Truncation   A.5.3(43), K(250)
S'Unbiased_Rounding   A.5.3(40), K(254)
S'Write   13.13.2(4), K(288)
S1   3.4(34), 12.3(22), 13.1(14), 13.4(11)
S2   13.1(14), 13.4(11)
safe range
   of a floating point type   3.5.7(9), 3.5.7(10)
safe separate compilation   10(3)
Safe_Convert   13.9.1(12)
Safe_First attribute   A.5.3(71), G.2.2(5), K(211)
Safe_Last attribute   A.5.3(72), G.2.2(6), K(213)
safety-critical systems   H(1)
Salary   3.5.9(28)
Salary_Conversions   B.4(108), B.4(120)
Salary_Type   B.4(105), B.4(114)
same value
   for a limited type   6.2(10)
Same_Denominator   7.2(11)
satisfies
   a discriminant constraint   3.7.1(11)
   a range constraint   3.5(4)
   an index constraint   3.6.1(7)
   for an access value   3.10(15)
Save   A.5.2(12), A.5.2(24)
Save_Occurrence   11.4.1(6)
Scalar type   3.2(2), 3.2(3), 3.5(1), N(37)
scalar_constraint   3.2.2(6)
   used   3.2.2(5), P(1)
scale
   of a decimal fixed point subtype   3.5.10(11), K(216)
Scale attribute   3.5.10(11), K(215)
Scaling attribute   A.5.3(27), K(217)
SCHAR_MAX   B.3(6)
SCHAR_MIN   B.3(6)
Schedule   3.6(28)
scope
   informal definition   3.1(8)
   of (a view of) an entity   8.2(11)
   of a use_clause   8.4(6)
   of a with_clause   10.1.2(5)
   of a declaration   8.2(10)
Seconds   9.6(13)
Seconds_Count   D.8(15)
Section_Sign   A.3.3(21)
secure systems   H(1)
Seize   9.4(27), 9.4(28), 9.5.2(33)
select an entry call
   from an entry queue   9.5.3(13), 9.5.3(16)
   immediately   9.5.3(8)
select_alternative   9.7.1(4)
   used   9.7.1(2), P(1)
select_statement   9.7(2)
   used   5.1(5), P(1)
selected_component   4.1.3(2)
   used   4.1(2), P(1)
selection
   of an entry caller   9.5.2(24)
selective_accept   9.7.1(2)
   used   9.7(2), P(1)
selector_name   4.1.3(3)
   used   3.7.1(3), 4.1.3(2), 4.3.1(5), 6.4(5), 12.3(4), P(1)
semantic dependence
   of one compilation unit upon another   10.1.1(26)
semicolon   2.1(15), A.3.3(10)
Send   13.13.2(40)
Sep   3.10.1(23)
separate compilation   10.1(1)
   safe   10(3)
separator   2.2(3)
Sequence   4.6(70)
sequence of characters
   of a string_literal   2.6(5)
sequence_of_statements   5.1(2)
   used   5.3(2), 5.4(3), 5.5(2), 9.7.1(2), 9.7.1(5), 9.7.1(6), 9.7.2(3),
        9.7.3(2), 9.7.4(3), 9.7.4(5), 11.2(2), 11.2(3), P(1)
sequential
   actions   9.10(11), C.6(17)
sequential access   A.8(2)
sequential file   A.8(1)
Sequential_IO   J.1(4)
   child of Ada   A.8.1(2)
Server   9.1(23), 9.7.1(24)
service
   an entry queue   9.5.3(13)
Set   3.9.3(15), 6.4(27), D.12(9), D.12(10)
Set_Col   A.10.1(35)
Set_Component   9.4(31), 9.4(33)
Set_Error   A.10.1(15)
Set_False   D.10(4)
Set_Index   A.8.4(14), A.12.1(22)
Set_Input   A.10.1(15)
Set_Line   A.10.1(36)
Set_Line_Length   A.10.1(23)
Set_Mask   13.8(13), 13.8(14)
Set_Mode   A.12.1(24)
Set_Output   A.10.1(15)
Set_Page_Length   A.10.1(24)
Set_Priority   D.5(4)
Set_True   D.10(4)
Set_Value   C.7.2(6)
Set_Im   G.1.1(7)
Set_Re   G.1.1(7)
Sets   3.9.3(15)
shared passive library unit   E.2(4), E.2.1(4)
shared variable
   protection of   9.10(1)
Shared_Array   9.4(31), 9.4(32)
Shared_Passive pragma   E.2.1(3), L(34)
Sharp   J.5(6)
shift   B.2(9)
Shift_Left   B.2(6)
Shift_Right   B.2(6)
Shift_Right_Arithmetic   B.2(6)
Short   13.3(82), B.3(7)
short-circuit control form   4.5.1(1)
Short_Float   3.5.7(16)
Short_Int   4.9(44)
Short_Integer   3.5.4(25)
Shut_Down   9.1(23)
SI   A.3.3(5)
Sigma   12.1(24), 12.2(12)
signal (an exception)
   See raise   11(1)
signal
   See interrupt   C.3(1)
   as defined between actions   9.10(2)
signal handling
   example   9.7.4(10)
signed integer type   3.5.4(1)
signed_char   B.3(8)
signed_integer_type_definition   3.5.4(3)
   used   3.5.4(2), P(1)
Signed_Zeros attribute   A.5.3(13), K(221)
simple entry call   9.5.3(1)
simple_expression   4.4(4)
   used   3.5(3), 3.5.4(3), 3.5.7(3), 4.4(3), 13.5.1(5), 13.5.1(6), P(1)
simple_statement   5.1(4)
   used   5.1(3), P(1)
Sin   A.5.1(5), G.1.2(4)
single
   class expected type   8.6(27)
single entry   9.5.2(20)
Single_Precision_Complex_Types   B.5(8)
single_protected_declaration   9.4(3)
   used   3.3.1(2), P(1)
single_task_declaration   9.1(3)
   used   3.3.1(2), P(1)
Singular   11.1(8)
Sinh   A.5.1(7), G.1.2(6)
size   A.8.4(15), A.12.1(23)
   of an object   13.1(7)
Size attribute   13.3(40), 13.3(45), K(223), K(228)
Size clause   13.3(7), 13.3(41), 13.3(48)
size_t   B.3(13)
Skip_Line   A.10.1(29)
Skip_Page   A.10.1(32)
slice   4.1.2(2), A.4.4(28), A.4.5(22)
   used   4.1(2), P(1)
small   13.3(48)
   of a fixed point type   3.5.9(8)
Small attribute   3.5.10(2), K(230)
Small clause   3.5.10(2), 13.3(7)
Small_Int   3.2.2(15), 3.5.4(35)
SO   A.3.3(5), J.5(4)
Soft_Hyphen   A.3.3(21)
SOH   A.3.3(5)
solidus   2.1(15), A.3.3(8)
Source   13.9(3)
SPA   A.3.3(18)
Space   A.3.3(8), A.4.1(4)
space_character   2.1(11)
   used   2.1(3), P(1)
special graphic character
   a category of Character   A.3.2(32)
special_character   2.1(12)
   used   2.1(3), P(1)
   names   2.1(15)
Special_Key   3.4(38)
Special_Set   A.4.6(4)
Specialized Needs Annexes   1.1.2(7)
specifiable (of an attribute and for an entity)   13.3(5)
specifiable
   of Address for entries   J.7.1(6)
   of Address for stand-alone objects and for program units   13.3(12)
   of Alignment for first subtypes and objects   13.3(25)
   of Bit_Order for record types and record extensions   13.5.3(4)
   of Component_Size for array types   13.3(70)
   of External_Tag for a tagged type   13.3(75), K(65)
   of Input for a type   13.13.2(36)
   of Machine_Radix for decimal first subtypes   F.1(1)
   of Output for a type   13.13.2(36)
   of Read for a type   13.13.2(36)
   of Size for first subtypes   13.3(48)
   of Size for stand-alone objects   13.3(41)
   of Small for fixed point types   3.5.10(2)
   of Storage_Pool for a non-derived access-to-object type   13.11(15)
   of Storage_Size for a task first subtype   J.9(3)
   of Storage_Size for a non-derived access-to-object type   13.11(15)
   of Write for a type   13.13.2(36)
specific type   3.4.1(3)
specified (not!)   1.1.3(18), M(1)
specified
   of an aspect of representation of an entity   13.1(17)
specified discriminant   3.7(18)
Spin   9.7.3(6)
Split   9.6(14), D.8(16)
Sqrt   A.5.1(4), B.1(51), G.1.2(3)
Square   3.2.2(15), 3.7(35), 12.3(24)
Squaring   12.1(22), 12.2(7)
squirrel away
   included in fairness to alligators   8.5.4(8)
SS2   A.3.3(17)
SS3   A.3.3(17)
SSA   A.3.3(17)
ST   A.3.3(19)
Stack   12.8(3), 12.8(4), 12.8(14)
Stack_Bool   12.8(10)
Stack_Int   12.8(10)
Stack_Real   12.8(16)
stand-alone constant   3.3.1(23)
   corresponding to a formal object of mode in   12.4(10)
stand-alone object   3.3.1(1)
stand-alone variable   3.3.1(23)
Standard   A.1(4)
standard error file   A.10(6)
standard input file   A.10(5)
standard mode   1.1.5(11)
standard output file   A.10(5)
standard storage pool   13.11(17)
Standard_Error   A.10.1(16), A.10.1(19)
Standard_Input   A.10.1(16), A.10.1(19)
Standard_Output   A.10.1(16), A.10.1(19)
State   3.8.1(24), 13.5.1(26), A.5.2(11), A.5.2(23), A.5.2(27)
State_Mask   13.5.1(27)
statement   5.1(3)
   used   5.1(2), P(1)
statement_identifier   5.1(8)
   used   5.1(7), 5.5(2), 5.6(2), P(1)
static   3.3.2(1), 4.9(1)
   constant   4.9(24)
   constraint   4.9(27)
   delta constraint   4.9(29)
   digits constraint   4.9(29)
   discrete_range   4.9(25)
   discriminant constraint   4.9(31)
   expression   4.9(2)
   function   4.9(18)
   index constraint   4.9(30)
   range   4.9(25)
   range constraint   4.9(29)
   scalar subtype   4.9(26)
   string subtype   4.9(26)
   subtype   4.9(26), 12.4(9)
   value   4.9(13)
static semantics   1.1.2(28)
statically
   constrained   4.9(32)
   denote   4.9(14)
statically compatible
   for a constraint and a scalar subtype   4.9.1(4)
   for a constraint and an access or composite subtype   4.9.1(4)
   for two subtypes   4.9.1(4)
statically deeper   3.10.2(4), 3.10.2(17)
statically determined tag   3.9.2(1)
   [partial]   3.9.2(15), 3.9.2(19)
statically matching
   effect on subtype-specific aspects   13.1(14)
   for constraints   4.9.1(1)
   for ranges   4.9.1(3)
   for subtypes   4.9.1(2)
   required   3.9.2(10), 3.10.2(27), 4.6(12), 4.6(16), 6.3.1(16), 6.3.1(17),
        6.3.1(23), 7.3(13), 12.5.1(14), 12.5.3(6), 12.5.3(7), 12.5.4(3),
        12.7(7)
statically tagged   3.9.2(4)
Status_Error   A.8.1(15), A.8.4(18), A.10.1(85), A.12.1(26), A.13(4)
storage deallocation
   unchecked   13.11.2(1)
storage element   13.3(8)
storage management
   user-defined   13.11(1)
storage node   E(2)
storage place
   of a component   13.5(1)
storage place attributes
   of a component   13.5.2(1)
storage pool   3.10(7)
storage pool element   13.11(11)
storage pool type   13.11(11)
Storage_Array   13.7.1(5)
Storage_Check   11.5(23)
   [partial]   11.1(6), 13.3(67), 13.11(17), D.7(15)
Storage_Count   13.7.1(4)
   subtype in package System.Storage_Elements   13.7.1(3)
Storage_Element   13.7.1(5)
Storage_Elements
   child of System   13.7.1(2)
Storage_Error   A.1(46)
   raised by failure of run-time check   4.8(14), 11.1(4), 11.1(6), 11.5(23),
        13.3(67), 13.11(17), 13.11(18), A.7(14), D.7(15)
Storage_Offset   13.7.1(3)
Storage_Pool attribute   13.11(13), K(232)
Storage_Pool clause   13.3(7), 13.11(15)
Storage_Pools
   child of System   13.11(5)
Storage_Size   13.11(9)
Storage_Size attribute   13.3(60), 13.11(14), J.9(2), K(234), K(236)
Storage_Size clause   13.3(7), 13.11(15)
   See also pragma Storage_Size   13.3(61)
Storage_Size pragma   13.3(63), L(35)
Storage_Unit   13.7(13)
   named number in package System   13.7(13)
Storage_IO
   child of Ada   A.9(3)
Str10   11.6(5)
Strcpy   B.3(78), B.3.2(48)
stream   13.13(1), A.12.1(13), A.12.2(4), A.12.3(4)
stream type   13.13(1)
Stream_Access   A.12.1(4), A.12.2(3), A.12.3(3)
Stream_Element   13.13.1(4)
Stream_Element_Array   13.13.1(4)
Stream_Element_Count   13.13.1(4)
Stream_Element_Offset   13.13.1(4)
Stream_IO
   child of Ada.Streams   A.12.1(3)
Streams
   child of Ada   13.13.1(2)
strict mode   G.2(1)
String   3.6.3(4), A.1(37)
string type   3.6.3(1)
String_Access   A.4.5(7)
string_element   2.6(3)
   used   2.6(2), P(1)
string_literal   2.6(2)
   used   4.4(7), 6.1(9), P(1)
Strings
   child of Ada   A.4.1(3)
   child of Interfaces.C   B.3.1(3)
Strlen   B.3.1(17)
structure
   See record type   3.8(1)
STS   A.3.3(18)
STX   A.3.3(5), J.5(4)
Sub   8.3(26), A.3.3(6), J.5(4)
subaggregate
   of an array_aggregate   4.3.3(6)
subcomponent   3.2(6)
subprogram   6(1)
   abstract   3.9.3(3)
subprogram call   6.4(1)
subprogram instance   12.3(13)
subprogram_body   6.3(2)
   used   3.11(6), 9.4(8), 10.1.1(7), P(1)
subprogram_body_stub   10.1.3(3)
   used   10.1.3(2), P(1)
subprogram_declaration   6.1(2)
   used   3.1(3), 9.4(5), 9.4(8), 10.1.1(5), P(1)
subprogram_default   12.6(3)
   used   12.6(2), P(1)
subprogram_renaming_declaration   8.5.4(2)
   used   8.5(2), 10.1.1(6), P(1)
subprogram_specification   6.1(4)
   used   6.1(2), 6.1(3), 6.3(2), 8.5.4(2), 10.1.3(3), 12.1(3), 12.6(2), P(1)
subsystem   10.1(3), N(22)
Subtraction   3.9.1(16)
subtype (of an object)
   See actual subtype of an object   3.3(23), 3.3.1(9)
Subtype   3.2(1), 3.2(8), N(38)
   of a generic formal object   12.4(10)
subtype conformance   6.3.1(17), 12.3(11)
   [partial]   3.10.2(34), 9.5.4(17)
   required   3.9.2(10), 3.10.2(32), 4.6(19), 8.5.4(5), 9.5.4(5), 13.3(6)
subtype conversion
   See also implicit subtype conversion   4.6(1)
   See type conversion   4.6(1)
subtype-specific
   attribute_definition_clause   13.3(7)
   of a representation item   13.1(8)
   of an aspect   13.1(8)
subtype_declaration   3.2.2(2)
   used   3.1(3), P(1)
subtype_indication   3.2.2(3)
   used   3.2.2(2), 3.3.1(2), 3.4(2), 3.6(6), 3.6(7), 3.6.1(3), 3.10(3),
        4.8(2), 7.3(3), P(1)
subtype_mark   3.2.2(4)
   used   3.2.2(3), 3.6(4), 3.7(5), 3.10(6), 4.3.2(3), 4.4(3), 4.6(2),
        4.7(2), 6.1(13), 6.1(15), 8.4(4), 8.5.1(2), 12.3(5), 12.4(2),
        12.5.1(3), 13.8(14), P(1)
subtypes
   of a profile   6.1(25)
subunit   10.1.3(7), 10.1.3(8)
   used   10.1.1(3), P(1)
Succ attribute   3.5(22), K(238)
Suit   3.5.1(14)
Sum   12.1(24), 12.2(10)
super
   See view conversion   4.6(5)
Superscript_One   A.3.3(22)
Superscript_Three   A.3.3(22)
Superscript_Two   A.3.3(22)
Suppress pragma   11.5(4), L(36)
suppressed check   11.5(8)
Suspend_Until_True   D.10(4)
Suspension_Object   D.10(4)
Swap   12.3(24)
Switch   6.1(37)
SYN   A.3.3(6), J.5(4)
synchronization   9(1)
Synchronous_Task_Control
   child of Ada   D.10(3)
syntactic category   1.1.4(15)
syntax
   complete listing   P(1)
   cross reference   P(1)
   notation   1.1.4(3)
   under Syntax heading   1.1.2(25)
System   13.7(3)
System.Address_To_Access_Conversions   13.7.2(2)
System.Machine_Code   13.8(7)
System.RPC   E.5(3)
System.Storage_Elements   13.7.1(2)
System.Storage_Pools   13.11(5)
System_Name   13.7(4)
systems programming   C(1)

T   3.4(38), 3.6(11), 3.9.1(4), 3.9.3(3), 3.9.3(10), 3.9.3(16), 3.10.2(22),
        7.3(7), 7.3(9), 7.5(2), 8.4(7), 8.5.4(8), 8.6(34), 9.4(20),
        9.5.2(13), 12.3(18), 13.5.1(12), 13.11(34), 13.14(1), 13.14(10),
        13.14(19), G.2.1(16)
T1   3.4(34), 3.9.2(20), 3.9.3(6), 3.10(9), 7.3(7), 7.6(11), 12.3(15),
        12.3(22), 13.4(11)
T2   3.4(34), 3.9.2(20), 3.9.3(6), 3.10(9), 7.3(7), 7.3(13), 7.3.1(7),
        7.6(11), 12.3(15), 12.3(22), 13.14(19)
T3   7.3.1(7)
T4   7.3.1(7)
T5   7.3.1(7)
Table   3.2.1(15), 3.6(28), 12.5(14), 12.5.3(11), 12.8(5), 12.8(14)
Tag   3.9(6)
Tag attribute   3.9(16), 3.9(18), K(242), K(244)
tag indeterminate   3.9.2(6)
tag of an object   3.9(3)
   class-wide object   3.9(22)
   object created by an allocator   3.9(21)
   preserved by type conversion and parameter passing   3.9(25)
   returned by a function   3.9(23), 3.9(24)
   stand-alone object, component, or aggregate   3.9(20)
Tag_Check   11.5(18)
   [partial]   3.9.2(16), 4.6(42), 4.6(52), 5.2(10), 6.5(9)
Tag_Error   3.9(8)
tagged type   3.9(2), N(39)
Tags
   child of Ada   3.9(6)
tail (of a queue)   D.2.1(5)
Tail   A.4.3(37), A.4.3(38), A.4.4(72), A.4.4(73), A.4.5(67), A.4.5(68)
Take   3.9.3(15)
Tan   A.5.1(5), G.1.2(4)
Tanh   A.5.1(7), G.1.2(6)
Tape   E.4.2(2)
Tape_Client   E.4.2(6)
Tape_Driver   E.4.2(4), E.4.2(5)
Tape_Ptr   E.4.2(3)
Tapes   E.4.2(2)
target   13.9(3)
   of an assignment_statement   5.2(3)
   of an assignment operation   5.2(3)
target entry
   of a requeue_statement   9.5.4(3)
target object
   of a requeue_statement   9.5(7)
   of a call on an entry or a protected subprogram   9.5(2)
target statement
   of a goto_statement   5.8(3)
target subtype
   of a type_conversion   4.6(3)
task   9(1)
   activation   9.2(1)
   completion   9.3(1)
   dependence   9.3(1)
   execution   9.2(1)
   termination   9.3(1)
task declaration   9.1(1)
task dispatching   D.2.1(4)
task dispatching point   D.2.1(4)
   [partial]   D.2.1(8), D.2.2(12)
task dispatching policy   9(10), D.2.2(6)
   [partial]   D.2.1(5)
task priority   D.1(15)
task state
   abnormal   9.8(4)
   blocked   9(10)
   callable   9.9(2)
   held   D.11(4)
   inactive   9(10)
   ready   9(10)
   terminated   9(10)
Task type   3.2(2), N(40)
task unit   9(9)
Task_Attributes
   child of Ada   C.7.2(2)
task_body   9.1(6)
   used   3.11(6), P(1)
task_body_stub   10.1.3(5)
   used   10.1.3(2), P(1)
task_definition   9.1(4)
   used   9.1(2), 9.1(3), P(1)
Task_Dispatching_Policy pragma   D.2.2(2), L(37)
Task_Identification
   child of Ada   C.7.1(2)
task_item   9.1(5)
   used   9.1(4), P(1)
task_type_declaration   9.1(2)
   used   3.2.1(3), P(1)
Task_ID   C.7.1(2)
Tasking_Error   A.1(46)
   raised by failure of run-time check   9.2(5), 9.5.3(21), 11.1(4),
        13.11.2(13), 13.11.2(14), C.7.2(13), D.5(8), D.11(8)
template   12(1)
   See generic unit   12(1)
   for a formal package   12.7(4)
term   4.4(5)
   used   4.4(4), P(1)
terminal interrupt
   example   9.7.4(10)
terminate_alternative   9.7.1(7)
   used   9.7.1(4), P(1)
terminated
   a task state   9(10)
Terminated attribute   9.9(3), K(246)
termination
   abnormal   10.2(25)
   normal   10.2(25)
   of a partition   10.2(25), E.1(7)
Terminator_Error   B.3(40)
Test   B.3(77)
Test_Call   B.4(102)
Test_External_Formats   B.4(111)
Test_Pointers   B.3.2(46)
tested type
   of a membership test   4.5.2(3)
text of a program   2.2(1)
Text_Streams
   child of Ada.Text_IO   A.12.2(3), A.12.3(3)
Text_IO   J.1(6)
   child of Ada   A.10.1(2)
throw (an exception)
   See raise   11(1)
thunk   13.14(19)
tick   2.1(15), 13.7(10), D.8(7)
   named number in package System   13.7(10)
Tilde   A.3.3(14)
Time   9.6(10), D.8(4)
time base   9.6(6)
time limit
   example   9.7.4(12)
time type   9.6(6)
Time-dependent Reset procedure
   of the random number generator   A.5.2(34)
time-out
   See asynchronous_select   9.7.4(12)
   See selective_accept   9.7.1(1)
   See timed_entry_call   9.7.2(1)
   example   9.7.4(12)
Time_Error   9.6(18)
Time_First   D.8(4)
Time_Last   D.8(4)
Time_Span   D.8(6)
Time_Span_First   D.8(6)
Time_Span_Last   D.8(6)
Time_Span_Unit   D.8(6)
Time_Span_Zero   D.8(6)
Time_Unit   D.8(4)
Time_Of   9.6(15), D.8(16)
timed_entry_call   9.7.2(2)
   used   9.7(2), P(1)
timer interrupt
   example   9.7.4(12)
times operator   4.4(1), 4.5.5(1)
timing
   See delay_statement   9.6(1)
TM   8.5.3(6)
To_Ada   B.3(22), B.3(26), B.3(28), B.3(32), B.3(37), B.3(39), B.4(17),
        B.4(19), B.5(13), B.5(14), B.5(16)
To_Address   13.7.1(10), 13.7.2(3)
To_Basic   A.3.2(6), A.3.2(7)
To_Binary   B.4(45), B.4(48)
To_Bounded_String   A.4.4(11)
To_Character   A.3.2(15)
To_COBOL   B.4(17), B.4(18)
To_Decimal   B.4(35), B.4(40), B.4(44), B.4(47)
To_Display   B.4(36)
To_Domain   A.4.2(24), A.4.7(24)
To_Duration   D.8(13)
To_Fortran   B.5(13), B.5(14), B.5(15)
To_Integer   13.7.1(10)
To_ISO_646   A.3.2(11), A.3.2(12)
To_Long_Binary   B.4(48)
To_Lower   A.3.2(6), A.3.2(7)
To_Mapping   A.4.2(23), A.4.7(23)
To_Packed   B.4(41)
To_Picture   F.3.3(6)
To_Pointer   13.7.2(3)
To_Range   A.4.2(24), A.4.7(25)
To_Ranges   A.4.2(10), A.4.7(10)
To_Sequence   A.4.2(19), A.4.7(19)
To_Set   A.4.2(8), A.4.2(9), A.4.2(17), A.4.2(18), A.4.7(8), A.4.7(9),
        A.4.7(17), A.4.7(18)
To_String   A.3.2(16), A.4.4(12), A.4.5(11)
To_Time_Span   D.8(13)
To_Unbounded_String   A.4.5(9), A.4.5(10)
To_Upper   A.3.2(6), A.3.2(7)
To_Wide_Character   A.3.2(17)
To_Wide_String   A.3.2(18)
To_C   B.3(21), B.3(25), B.3(27), B.3(32), B.3(36), B.3(38)
token
   See lexical element   2.2(1)
Tolerance   3.3.1(33)
Trailing_Nonseparate   B.4(23)
Trailing_Separate   B.4(23)
transfer of control   5.1(14)
Translate   A.4.3(18), A.4.3(19), A.4.3(20), A.4.3(21), A.4.4(53), A.4.4(54),
        A.4.4(55), A.4.4(56), A.4.5(48), A.4.5(49), A.4.5(50), A.4.5(51)
Traverse_Tree   6.1(37)
triggering_alternative   9.7.4(3)
   used   9.7.4(2), P(1)
triggering_statement   9.7.4(4)
   used   9.7.4(3), P(1)
Trim   A.4.3(31), A.4.3(32), A.4.3(33), A.4.3(34), A.4.4(67), A.4.4(68),
        A.4.4(69), A.4.5(61), A.4.5(62), A.4.5(63), A.4.5(64)
Trim_End   A.4.1(6)
True   3.5.3(1)
Truncation   A.4.1(6)
Truncation attribute   A.5.3(42), K(248)
TT   3.9.1(4)
two's complement
   modular types   3.5.4(29)
Two_Discrims   7.3(13)
Two_Pi   3.3.2(9)
type   3.2(1), N(41)
   See also tag   3.9(3)
   abstract   3.9.3(2)
   See also   language-defined types
type conformance   6.3.1(15)
   [partial]   3.4(17), 8.3(8), 8.3(26), 10.1.4(4)
   required   3.11.1(5), 4.1.4(14), 8.6(26), 9.5.4(3)
type conversion   4.6(1)
   See also qualified_expression   4.7(1)
   access   4.6(13), 4.6(18), 4.6(47)
   arbitrary order   1.1.4(18)
   array   4.6(9), 4.6(36)
   composite (non-array)   4.6(21), 4.6(40)
   enumeration   4.6(21), 4.6(34)
   numeric   4.6(8), 4.6(29)
   unchecked   13.9(1)
type conversion, implicit
   See implicit subtype conversion   4.6(1)
type extension   3.9(2), 3.9.1(1)
type of a discrete_range   3.6.1(4)
type of a range   3.5(4)
type parameter
   See discriminant   3.7(1)
type profile
   See profile, type conformant   6.3.1(15)
type resolution rules   8.6(20)
   if any type in a specified class of types is expected   8.6(21)
   if expected type is specific   8.6(22)
   if expected type is universal or class-wide   8.6(21)
type tag
   See tag   3.9(3)
type-related
   aspect   13.1(8)
   attribute_definition_clause   13.3(7)
   representation item   13.1(8)
type_conversion   4.6(2)
   used   4.1(2), P(1)
   See also unchecked type conversion   13.9(1)
type_declaration   3.2.1(2)
   used   3.1(3), P(1)
type_definition   3.2.1(4)
   used   3.2.1(3), P(1)
Type_Set   A.10.1(7), A.10.10(3)
types
   of a profile   6.1(29)

UC_Icelandic_Eth   A.3.3(24)
UC_Icelandic_Thorn   A.3.3(24)
UC_A_Acute   A.3.3(23)
UC_A_Circumflex   A.3.3(23)
UC_A_Diaeresis   A.3.3(23)
UC_A_Grave   A.3.3(23)
UC_A_Ring   A.3.3(23)
UC_A_Tilde   A.3.3(23)
UC_AE_Diphthong   A.3.3(23)
UC_C_Cedilla   A.3.3(23)
UC_E_Acute   A.3.3(23)
UC_E_Circumflex   A.3.3(23)
UC_E_Diaeresis   A.3.3(23)
UC_E_Grave   A.3.3(23)
UC_I_Acute   A.3.3(23)
UC_I_Circumflex   A.3.3(23)
UC_I_Diaeresis   A.3.3(23)
UC_I_Grave   A.3.3(23)
UC_N_Tilde   A.3.3(24)
UC_O_Acute   A.3.3(24)
UC_O_Circumflex   A.3.3(24)
UC_O_Diaeresis   A.3.3(24)
UC_O_Grave   A.3.3(24)
UC_O_Oblique_Stroke   A.3.3(24)
UC_O_Tilde   A.3.3(24)
UC_U_Acute   A.3.3(24)
UC_U_Circumflex   A.3.3(24)
UC_U_Diaeresis   A.3.3(24)
UC_U_Grave   A.3.3(24)
UC_Y_Acute   A.3.3(24)
UCHAR_MAX   B.3(6)
UI   1.3(1)
ultimate ancestor
   of a type   3.4.1(10)
unary adding operator   4.5.4(1)
unary operator   4.5(9)
unary_adding_operator   4.5(5)
   used   4.4(4), P(1)
Unbiased_Rounding attribute   A.5.3(39), K(252)
Unbounded   A.10.1(5)
   child of Ada.Strings   A.4.5(3)
Unbounded_String   A.4.5(4)
unchecked storage deallocation   13.11.2(1)
unchecked type conversion   13.9(1)
Unchecked_Access attribute   13.10(3), H.4(18), K(256)
   See also Access attribute   3.10.2(24)
Unchecked_Conversion   J.1(2)
   child of Ada   13.9(3)
Unchecked_Deallocation   J.1(3)
   child of Ada   13.11.2(3)
unconstrained   3.2(9)
   object   3.3.1(9), 3.10(9), 6.4.1(16)
   subtype   3.2(9), 3.4(6), 3.5(7), 3.5.1(10), 3.5.4(9), 3.5.4(10),
        3.5.7(11), 3.5.9(13), 3.5.9(16), 3.6(15), 3.6(16), 3.7(26), 3.9(15),
        3.10(14), K(33)
unconstrained_array_definition   3.6(3)
   used   3.6(2), P(1)
undefined result   11.6(5)
underline   2.1(15), J.5(6)
   used   2.3(2), 2.4.1(3), 2.4.2(4), P(1)
Uniformity Issue (UI)   1.3(1)
Uniformity Rapporteur Group (URG)   1.3(1)
Uniformly_Distributed   A.5.2(8)
uninitialized allocator   4.8(4)
uninitialized variables   13.9.1(2)
   [partial]   3.3.1(21), 13.3(55)
Union   3.9.3(15)
unit consistency   E.3(6)
Unit_Set   3.9.3(15)
universal type   3.4.1(6)
universal_fixed
   [partial]   3.5.6(4)
universal_integer   3.5.4(30)
   [partial]   3.5.4(14)
universal_real
   [partial]   3.5.6(4)
unknown discriminants   3.7(26)
   [partial]   3.7(1)
unknown_discriminant_part   3.7(3)
   used   3.7(2), P(1)
unmarshalling   E.4(9)
unpolluted   13.13.1(2)
Unrelated   7.3.1(7)
Unsafe_Convert   13.9.1(12)
unsigned   B.3(9), B.4(23)
unsigned type
   See modular type   3.5.4(1)
Unsigned_   B.2(5)
unsigned_char   B.3(10)
unsigned_long   B.3(9)
unsigned_short   B.3(9)
unspecified   1.1.3(18), M(1)
   [partial]   2.1(5), 4.5.2(13), 4.5.5(21), 6.2(11), 7.2(5), 9.8(14),
        10.2(26), 11.1(6), 11.5(27), 13.1(18), 13.7.2(5), 13.9.1(7),
        13.11(20), A.1(1), A.5.1(34), A.5.2(28), A.5.2(34), A.7(6), A.10(8),
        A.10.7(8), A.10.7(12), A.10.7(19), A.14(1), A.15(20), D.2.2(6),
        D.8(19), G.1.1(40), G.1.2(33), G.1.2(48), H(4), H.2(1)
Up_To_K   3.2.2(15)
update   B.3.1(18), B.3.1(19)
   the value of an object   3.3(14)
Update_Error   B.3.1(20)
upper bound
   of a range   3.5(4)
upper-case letter
   a category of Character   A.3.2(26)
upper_case_identifier_letter   2.1(8)
Upper_Case_Map   A.4.6(5)
Upper_Set   A.4.6(4)
URG   1.3(1)
US   A.3.3(6)
usage name   3.1(10)
use-visible   8.3(4), 8.4(9)
use_clause   8.4(2)
   used   3.11(4), 10.1.2(3), 12.1(5), P(1)
Use_Error   A.8.1(15), A.8.4(18), A.10.1(85), A.12.1(26), A.13(4)
use_package_clause   8.4(3)
   used   8.4(2), P(1)
use_type_clause   8.4(4)
   used   8.4(2), P(1)
User   9.1(28)
user-defined assignment   7.6(1)
user-defined heap management   13.11(1)
user-defined operator   6.6(1)
user-defined storage management   13.11(1)
User_Defined_Equal   8.5.4(8)

Val attribute   3.5.5(5), K(258)
Valid   B.4(33), B.4(38), B.4(43), F.3.3(5), F.3.3(12)
Valid attribute   13.9.2(3), H(6), K(262)
value   3.2(10), A.4.2(21), A.5.2(14), A.5.2(26), B.3.1(13), B.3.1(14),
        B.3.1(15), B.3.1(16), B.3.2(6), B.3.2(7), C.7.2(4)
Value attribute   3.5(52), K(264)
value conversion   4.6(5)
Var_Line   3.6.1(17)
variable   3.3(13)
variable object   3.3(13)
variable view   3.3(13)
variant   3.8.1(3)
   used   3.8.1(2), P(1)
   See also tagged type   3.9(1)
variant_part   3.8.1(2)
   used   3.8(4), P(1)
Vector   3.6(26), 12.1(24), 12.5.3(11)
version
   of a compilation unit   E.3(5)
Version attribute   E.3(3), K(268)
vertical line   2.1(15)
Vertical_Line   A.3.3(14)
view   3.1(7), N(12), N(42)
view conversion   4.6(5)
virtual function
   See dispatching subprogram   3.9.2(1)
Virtual_Length   B.3.2(13)
visibility
   direct   8.3(2), 8.3(21)
   immediate   8.3(4), 8.3(21)
   use clause   8.3(4), 8.4(9)
visibility rules   8.3(1)
visible   8.3(2), 8.3(14)
   within a pragma in a context_clause   10.1.6(3)
   within a pragma that appears at the place of a compilation unit
        10.1.6(5)
   within a with_clause   10.1.6(2)
   within a use_clause in a context_clause   10.1.6(3)
   within the parent_unit_name of a library unit   10.1.6(2)
   within the parent_unit_name of a subunit   10.1.6(4)
visible part   8.2(5)
   of a formal package   12.7(10)
   of a generic unit   8.2(8)
   of a package (other than a generic formal package)   7.1(6)
   of a protected unit   9.4(11)
   of a task unit   9.1(9)
   of a view of a callable entity   8.2(6)
   of a view of a composite type   8.2(7)
   of an instance   12.3(12)
volatile   C.6(8)
Volatile pragma   C.6(4), L(38)
Volatile_Components pragma   C.6(6), L(39)
Volt   3.5.9(26)
VT   A.3.3(5)
VTS   A.3.3(17)

wchar_t   B.3(30)
Weekday   3.5.1(16)
well-formed picture String
   for edited output   F.3.1(1)
Wide_Bounded
   child of Ada.Strings   A.4.7(1)
Wide_Character   3.5.2(3), A.1(36)
Wide_Character_Mapping   A.4.7(20)
Wide_Character_Mapping_Function   A.4.7(26)
Wide_Character_Range   A.4.7(6)
Wide_Character_Sequence   A.4.7(16)
Wide_Character_Set   A.4.7(4)
Wide_Constants
   child of Ada.Strings.Wide_Maps   A.4.7(1)
Wide_Fixed
   child of Ada.Strings   A.4.7(1)
Wide_Image attribute   3.5(28), K(270)
Wide_Maps
   child of Ada.Strings   A.4.7(3)
wide_nul   B.3(31)
Wide_Space   A.4.1(4)
Wide_String   3.6.3(4), A.1(41)
Wide_Text_IO
   child of Ada   A.11(2)
Wide_Unbounded
   child of Ada.Strings   A.4.7(1)
Wide_Value attribute   3.5(40), K(274)
Wide_Width attribute   3.5(38), K(278)
Width attribute   3.5(39), K(280)
with_clause   10.1.2(4)
   used   10.1.2(3), P(1)
   mentioned in   10.1.2(6)
within
   immediately   8.1(13)
word   13.3(8), 13.5.1(25)
Word_Size   13.7(13)
   named number in package System   13.7(13)
wording changes from Ada 83   1.1.2(39)
Worker   A.5.2(60)
Write   7.5(19), 7.5(20), 9.1(24), 9.11(8), 9.11(9), 13.13.1(6), 13.13.2(40),
        A.8.1(12), A.8.4(13), A.9(7), A.12.1(18), A.12.1(19), E.5(8)
Write attribute   13.13.2(3), 13.13.2(11), K(282), K(286)
Write clause   13.3(7), 13.13.2(36)

X   4.9(37), 8.2(3), 8.2(12), 8.3(29), 13.5.1(12)
xor operator   4.4(1), 4.5.1(2)

Y   3.10.2(22), 13.1(22)
Year   9.6(13)
Year_Number   9.6(11)
Yen_Sign   A.3.3(21)
Contents

Foreword

Introduction

1. General

   1.1 Scope
       1.1.1 Extent
       1.1.2 Structure
       1.1.3 Conformity of an Implementation with the Standard
       1.1.4 Method of Description and Syntax Notation
       1.1.5 Classification of Errors
   1.2 Normative References
   1.3 Definitions

2. Lexical Elements

   2.1 Character Set
   2.2 Lexical Elements, Separators, and Delimiters
   2.3 Identifiers
   2.4 Numeric Literals
       2.4.1 Decimal Literals
       2.4.2 Based Literals
   2.5 Character Literals
   2.6 String Literals
   2.7 Comments
   2.8 Pragmas
   2.9 Reserved Words

3. Declarations and Types

   3.1 Declarations
   3.2 Types and Subtypes
       3.2.1 Type Declarations
       3.2.2 Subtype Declarations
       3.2.3 Classification of Operations
   3.3 Objects and Named Numbers
       3.3.1 Object Declarations
       3.3.2 Number Declarations
   3.4 Derived Types and Classes
       3.4.1 Derivation Classes









Copyright (C) 1992,1993,1994,1995  Intermetrics, Inc.

This copyright is assigned to the U.S. Government.  All rights reserved.

This document may be copied, in whole or in part, in any form or by any
means, as is or with alterations, provided that (1) alterations are clearly
marked as alterations and (2) this copyright notice is included unmodified in
any copy.  Compiled copies of standard library units and examples need not
contain this copyright notice so long as the notice is included in all copies
of source code and documentation.
   3.5 Scalar Types
       3.5.1 Enumeration Types
       3.5.2 Character Types
       3.5.3 Boolean Types
       3.5.4 Integer Types
       3.5.5 Operations of Discrete Types
       3.5.6 Real Types
       3.5.7 Floating Point Types
       3.5.8 Operations of Floating Point Types
       3.5.9 Fixed Point Types
       3.5.10 Operations of Fixed Point Types
   3.6 Array Types
       3.6.1 Index Constraints and Discrete Ranges
       3.6.2 Operations of Array Types
       3.6.3 String Types
   3.7 Discriminants
       3.7.1 Discriminant Constraints
       3.7.2 Operations of Discriminated Types
   3.8 Record Types
       3.8.1 Variant Parts and Discrete Choices
   3.9 Tagged Types and Type Extensions
       3.9.1 Type Extensions
       3.9.2 Dispatching Operations of Tagged Types
       3.9.3 Abstract Types and Subprograms
   3.10 Access Types
       3.10.1 Incomplete Type Declarations
       3.10.2 Operations of Access Types
   3.11 Declarative Parts
       3.11.1 Completions of Declarations

4. Names and Expressions

   4.1 Names
       4.1.1 Indexed Components
       4.1.2 Slices
       4.1.3 Selected Components
       4.1.4 Attributes
   4.2 Literals
   4.3 Aggregates
       4.3.1 Record Aggregates
       4.3.2 Extension Aggregates
       4.3.3 Array Aggregates
   4.4 Expressions
   4.5 Operators and Expression Evaluation
       4.5.1 Logical Operators and Short-circuit Control Forms
       4.5.2 Relational Operators and Membership Tests
       4.5.3 Binary Adding Operators
       4.5.4 Unary Adding Operators
       4.5.5 Multiplying Operators
       4.5.6 Highest Precedence Operators
   4.6 Type Conversions
   4.7 Qualified Expressions
   4.8 Allocators
   4.9 Static Expressions and Static Subtypes
       4.9.1 Statically Matching Constraints and Subtypes

5. Statements

   5.1 Simple and Compound Statements - Sequences of Statements
   5.2 Assignment Statements
   5.3 If Statements
   5.4 Case Statements
   5.5 Loop Statements
   5.6 Block Statements
   5.7 Exit Statements
   5.8 Goto Statements

6. Subprograms

   6.1 Subprogram Declarations
   6.2 Formal Parameter Modes
   6.3 Subprogram Bodies
       6.3.1 Conformance Rules
       6.3.2 Inline Expansion of Subprograms
   6.4 Subprogram Calls
       6.4.1 Parameter Associations
   6.5 Return Statements
   6.6 Overloading of Operators

7. Packages

   7.1 Package Specifications and Declarations
   7.2 Package Bodies
   7.3 Private Types and Private Extensions
       7.3.1 Private Operations
   7.4 Deferred Constants
   7.5 Limited Types
   7.6 User-Defined Assignment and Finalization
       7.6.1 Completion and Finalization

8. Visibility Rules

   8.1 Declarative Region
   8.2 Scope of Declarations
   8.3 Visibility
   8.4 Use Clauses
   8.5 Renaming Declarations
       8.5.1 Object Renaming Declarations
       8.5.2 Exception Renaming Declarations
       8.5.3 Package Renaming Declarations
       8.5.4 Subprogram Renaming Declarations
       8.5.5 Generic Renaming Declarations
   8.6 The Context of Overload Resolution

9. Tasks and Synchronization

   9.1 Task Units and Task Objects
   9.2 Task Execution - Task Activation
   9.3 Task Dependence - Termination of Tasks
   9.4 Protected Units and Protected Objects
   9.5 Intertask Communication
       9.5.1 Protected Subprograms and Protected Actions
       9.5.2 Entries and Accept Statements
       9.5.3 Entry Calls
       9.5.4 Requeue Statements
   9.6 Delay Statements, Duration, and Time
   9.7 Select Statements
       9.7.1 Selective Accept
       9.7.2 Timed Entry Calls
       9.7.3 Conditional Entry Calls
       9.7.4 Asynchronous Transfer of Control
   9.8 Abort of a Task - Abort of a Sequence of Statements
   9.9 Task and Entry Attributes
   9.10 Shared Variables
   9.11 Example of Tasking and Synchronization

10. Program Structure and Compilation Issues

   10.1 Separate Compilation
       10.1.1 Compilation Units - Library Units
       10.1.2 Context Clauses - With Clauses
       10.1.3 Subunits of Compilation Units
       10.1.4 The Compilation Process
       10.1.5 Pragmas and Program Units
       10.1.6 Environment-Level Visibility Rules
   10.2 Program Execution
       10.2.1 Elaboration Control

11. Exceptions

   11.1 Exception Declarations
   11.2 Exception Handlers
   11.3 Raise Statements
   11.4 Exception Handling
       11.4.1 The Package Exceptions
       11.4.2 Example of Exception Handling
   11.5 Suppressing Checks
   11.6 Exceptions and Optimization

12. Generic Units

   12.1 Generic Declarations
   12.2 Generic Bodies
   12.3 Generic Instantiation
   12.4 Formal Objects
   12.5 Formal Types
       12.5.1 Formal Private and Derived Types
       12.5.2 Formal Scalar Types
       12.5.3 Formal Array Types
       12.5.4 Formal Access Types
   12.6 Formal Subprograms
   12.7 Formal Packages
   12.8 Example of a Generic Package

13. Representation Issues

   13.1 Representation Items
   13.2 Pragma Pack
   13.3 Representation Attributes
   13.4 Enumeration Representation Clauses
   13.5 Record Layout
       13.5.1 Record Representation Clauses
       13.5.2 Storage Place Attributes
       13.5.3 Bit Ordering
   13.6 Change of Representation
   13.7 The Package System
       13.7.1 The Package System.Storage_Elements
       13.7.2 The Package System.Address_To_Access_Conversions
   13.8 Machine Code Insertions
   13.9 Unchecked Type Conversions
       13.9.1 Data Validity
       13.9.2 The Valid Attribute
   13.10 Unchecked Access Value Creation
   13.11 Storage Management
       13.11.1 The Max_Size_In_Storage_Elements Attribute
       13.11.2 Unchecked Storage Deallocation
       13.11.3 Pragma Controlled
   13.12 Pragma Restrictions
   13.13 Streams
       13.13.1 The Package Streams
       13.13.2 Stream-Oriented Attributes
   13.14 Freezing Rules
ANNEXES



A. Predefined Language Environment

   A.1 The Package Standard
   A.2 The Package Ada
   A.3 Character Handling
       A.3.1 The Package Characters
       A.3.2 The Package Characters.Handling
       A.3.3 The Package Characters.Latin_1
   A.4 String Handling
       A.4.1 The Package Strings
       A.4.2 The Package Strings.Maps
       A.4.3 Fixed-Length String Handling
       A.4.4 Bounded-Length String Handling
       A.4.5 Unbounded-Length String Handling
       A.4.6 String-Handling Sets and Mappings
       A.4.7 Wide_String Handling
   A.5 The Numerics Packages
       A.5.1 Elementary Functions
       A.5.2 Random Number Generation
       A.5.3 Attributes of Floating Point Types
       A.5.4 Attributes of Fixed Point Types
   A.6 Input-Output
   A.7 External Files and File Objects
   A.8 Sequential and Direct Files
       A.8.1 The Generic Package Sequential_IO
       A.8.2 File Management
       A.8.3 Sequential Input-Output Operations
       A.8.4 The Generic Package Direct_IO
       A.8.5 Direct Input-Output Operations
   A.9 The Generic Package Storage_IO
   A.10 Text Input-Output
       A.10.1 The Package Text_IO
       A.10.2 Text File Management
       A.10.3 Default Input, Output, and Error Files
       A.10.4 Specification of Line and Page Lengths
       A.10.5 Operations on Columns, Lines, and Pages
       A.10.6 Get and Put Procedures
       A.10.7 Input-Output of Characters and Strings
       A.10.8 Input-Output for Integer Types
       A.10.9 Input-Output for Real Types
       A.10.10 Input-Output for Enumeration Types
   A.11 Wide Text Input-Output
   A.12 Stream Input-Output
       A.12.1 The Package Streams.Stream_IO
       A.12.2 The Package Text_IO.Text_Streams
       A.12.3 The Package Wide_Text_IO.Text_Streams
   A.13 Exceptions in Input-Output
   A.14 File Sharing
   A.15 The Package Command_Line

B. Interface to Other Languages

   B.1 Interfacing Pragmas
   B.2 The Package Interfaces
   B.3 Interfacing with C
       B.3.1 The Package Interfaces.C.Strings
       B.3.2 The Generic Package Interfaces.C.Pointers
   B.4 Interfacing with COBOL
   B.5 Interfacing with Fortran

C. Systems Programming

   C.1 Access to Machine Operations
   C.2 Required Representation Support
   C.3 Interrupt Support
       C.3.1 Protected Procedure Handlers
       C.3.2 The Package Interrupts
   C.4 Preelaboration Requirements
   C.5 Pragma Discard_Names
   C.6 Shared Variable Control
   C.7 Task Identification and Attributes
       C.7.1 The Package Task_Identification
       C.7.2 The Package Task_Attributes

D. Real-Time Systems

   D.1 Task Priorities
   D.2 Priority Scheduling
       D.2.1 The Task Dispatching Model
       D.2.2 The Standard Task Dispatching Policy
   D.3 Priority Ceiling Locking
   D.4 Entry Queuing Policies
   D.5 Dynamic Priorities
   D.6 Preemptive Abort
   D.7 Tasking Restrictions
   D.8 Monotonic Time
   D.9 Delay Accuracy
   D.10 Synchronous Task Control
   D.11 Asynchronous Task Control
   D.12 Other Optimizations and Determinism Rules

E. Distributed Systems

   E.1 Partitions
   E.2 Categorization of Library Units
       E.2.1 Shared Passive Library Units
       E.2.2 Remote Types Library Units
       E.2.3 Remote Call Interface Library Units
   E.3 Consistency of a Distributed System
   E.4 Remote Subprogram Calls
       E.4.1 Pragma Asynchronous
       E.4.2 Example of Use of a Remote Access-to-Class-Wide Type
   E.5 Partition Communication Subsystem

F. Information Systems

   F.1 Machine_Radix Attribute Definition Clause
   F.2 The Package Decimal
   F.3 Edited Output for Decimal Types
       F.3.1 Picture String Formation
       F.3.2 Edited Output Generation
       F.3.3 The Package Text_IO.Editing
       F.3.4 The Package Wide_Text_IO.Editing

G. Numerics

   G.1 Complex Arithmetic
       G.1.1 Complex Types
       G.1.2 Complex Elementary Functions
       G.1.3 Complex Input-Output
       G.1.4 The Package Wide_Text_IO.Complex_IO
   G.2 Numeric Performance Requirements
       G.2.1 Model of Floating Point Arithmetic
       G.2.2 Model-Oriented Attributes of Floating Point Types
       G.2.3 Model of Fixed Point Arithmetic
       G.2.4 Accuracy Requirements for the Elementary Functions
       G.2.5 Performance Requirements for Random Number Generation
       G.2.6 Accuracy Requirements for Complex Arithmetic

H. Safety and Security

   H.1 Pragma Normalize_Scalars
   H.2 Documentation of Implementation Decisions
   H.3 Reviewable Object Code
       H.3.1 Pragma Reviewable
       H.3.2 Pragma Inspection_Point
   H.4 Safety and Security Restrictions

J. Obsolescent Features

   J.1 Renamings of Ada 83 Library Units
   J.2 Allowed Replacements of Characters
   J.3 Reduced Accuracy Subtypes
   J.4 The Constrained Attribute
   J.5 ASCII
   J.6 Numeric_Error
   J.7 At Clauses
       J.7.1 Interrupt Entries
   J.8 Mod Clauses
   J.9 The Storage_Size Attribute

K. Language-Defined Attributes

L. Language-Defined Pragmas

M. Implementation-Defined Characteristics

N. Glossary

P. Syntax Summary

Index